62-303.720 Delisting Procedure.

(1) Waters on planning lists developed under this chapter that are verified to not be impaired during development of the verified list shall be removed from the State’s planning list. Once a water segment is verified to not be impaired pursuant to Part III of this chapter, the data used to place the water on the planning list shall not be the sole basis for listing that water segment on future planning lists.

(2) Water segments shall be removed from the State’s verified list only after completion of a TMDL for all pollutants causing impairment of the segment or upon demonstration that the water meets the water quality standard that was previously established as not being met.

(a) For waters listed due to failure to meet aquatic life use support based on water quality criteria exceedances or due to threats to human health based on exceedances of single sample water quality criteria, the water shall be delisted when:

1. The number of exceedances of an applicable water quality criterion due to pollutant discharges is less than or equal to the number listed in Table 3 for the given sample size, with a minimum sample size of 30. This table provides the number of exceedances that indicate a maximum of a 10% exceedance frequency with a minimum of a 90% confidence level using a binomial distribution, or

2. Following implementation of pollution control activities that are expected to be sufficient to result in attainment of applicable water quality standards, evaluation of new data indicates the water no longer meets the criteria for listing established in Rule 62-303.420, F.A.C., or

3. Following demonstration that the water was inappropriately listed due to flaws in the original analysis, evaluation of available data indicates the water does not meet the criteria for listing established in Rule 62-303.420, F.A.C.

New data evaluated under subparagraph 62-303.720(2)(a)1., F.A.C., must meet the following requirements:

a. They must include samples collected during similar conditions (same seasons and general flow conditions) that the data previously used to determine impairment were collected, with no more than 50% of the samples collected in any one quarter,

b. The sample size must be a minimum of 30 samples, and

c. The data must meet the requirements of subsections 62-303.320(4), (6) and (7), F.A.C.

(b) For waters listed due to failure to meet aquatic life use support based on biological data, the water shall be delisted when the segment passes two independent follow-up bioassessments and there have been no failed bioassessments for at least one year. The follow-up tests must meet the following requirements:

1. For streams, the new data may be two BioRecons or any combination of BioRecons and SCIs.

2. The bioassessments must be conducted during similar conditions (same seasons and general flow conditions) under which the previous bioassessments used to determine impairment were collected.

3. The data must meet the requirements of subsections 62-303.330(1) and (2), F.A.C.

(c) For waters listed due to failure to meet aquatic life use support based on toxicity data, the water shall be delisted when the segment passes two independent follow-up toxicity tests and there have been no failed toxicity tests for at least one year. The follow-up tests must meet the following requirements:

1. The tests must be conducted using the same test protocols and during similar conditions (same seasons and general flow conditions) under which the previous test used to determine impairment were collected.

2. The data must meet the requirements of subsection 62-303.340(1), F.A.C., and the time requirements of subsections 62-303.340(2) or (3), F.A.C.

(d) For waters listed due to fish consumption advisories, the water shall be delisted following the lifting of the advisory or when data complying with paragraphs 62-303.470(1)(a) and (b), F.A.C., demonstrate that the continuation of the advisory is no longer appropriate.

(e) For waters listed due to changes in shellfish bed management classification, the water shall be delisted upon reclassification of the shellfish harvesting area to its original or higher harvesting classification. Reclassification of a water from prohibited to unclassified does not constitute a higher classification.

(f) For waters listed due to bathing area closure or advisory data, the water shall be delisted if the bathing area does not meet the listing thresholds in subsection 62-303.360(1), F.A.C., for five consecutive years.

(g) For waters listed based on impacts to potable water supplies, the water shall be delisted when applicable water quality criteria are met as defined in paragraph 62-303.380(1)(a), F.A.C., and when the causes resulting in higher treatment costs have been ameliorated.

(h) For waters listed based on exceedance of a human health-based annual average criterion, the water shall be delisted when the annual average concentration is less than the criterion for three consecutive years.

(i) For waters listed based on nutrient impairment, the water shall be delisted if it does not meet the listing thresholds in Rule 62-303.450, F.A.C., for three consecutive years.

(j) For any listed water, the water shall be delisted if, following a change in approved analytical procedures, criteria, or water quality standards, evaluation of available data indicates the water no longer meets the applicable criteria for listing.

| Table 3: Delisting |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |

Maximum number of measured exceedances allowable to DELIST with at least 90% confidence that the actual exceedance rate is less than ten percent.

| Sample Sizes |  | Maximum # of exceedances allowable for delisting |  | Sample Sizes |  | Maximum # of exceedances allowable for delisting |
| --- | --- | --- | --- | --- | --- | --- |
| From | To |  |  | From | To |  |
| 30 | 37 | 0 |  | 279 | 289 | 21 |