## 14-60.009 Airspace Protection.

(1) Airspace Obstruction Permit.

(a) Any person proposing the erection, alteration, or modification of any structure that would exceed federal obstruction standards and which lies within the Department’s jurisdictional area of responsibility is required to obtain an airspace obstruction permit from the Department. However, such airspace obstruction permits shall be required only where the proposed site is within a ten nautical mile radius of the geographical center of a publicly owned or operated airport, a military airport, or an airport licensed by the state for public use.

(b) An Airspace Obstruction Permit Application, DOT Form 725-040-11, Rev. 02/04, incorporated by reference under Rule 14-60.011, F.A.C., with all required supporting documentation shall be submitted to: Airspace and Land Use Manager, Florida Department of Transportation, 605 Suwannee Street, MS #46, Tallahassee, Florida 32399-0450.

(c) In determining whether to issue a permit, the Department shall consider:

1. The nature of the terrain and height of existing structures.

2. Public and private interests and investments.

3. The character of flying operations and planned developments of airports.

4. Federal airways as designated by the Federal Aviation Administration.

5. Whether the construction of the proposed structure would cause an increase in the minimum descent altitude or the decision height at the affected airport.

6. Technological advances.

7. The safety of persons on the ground and in the air.

8. Land use density.

9. The safe and efficient use of navigable airspace.

10. The cumulative effects on navigable airspace of all existing structures, proposed structures identified in the applicable jurisdictions’ comprehensive plans, and all other known proposed structures in the area.

(d) The Department shall not approve an airspace obstruction permit unless the applicant submits documentation showing compliance with the federal requirement for notification of proposed construction and a valid FAA aeronautical determination. No permit shall be approved solely on the basis that the proposed structure will not exceed federal obstruction or any other federal aviation regulation.

(e) Any airspace obstruction permit granted by the Department shall require the applicant’s compliance with obstruction marking and lighting standards contained herein.

(2) Local Government Ordinance. Any local government airport zoning ordinance, concerning airport hazards, adopted in accordance with Chapter 333, F.S., shall require obstruction marking and lighting in compliance with the marking and lighting standards set forth in this rule chapter.

(3) Local Government Variance. Any person filing a request with a local government for a variance from an airport zoning ordinance in order to erect any structure, or increase the height of any structure, or permit the growth of any tree, or otherwise use property contrary to the airport zoning regulations shall forward a copy of the application to the Department by certified mail to the Airspace and Land Use Manager at the Department address in paragraph 14-60.009(1)(b), F.A.C., above.

(a) The Department shall review the application for local government variance, file a response or waive the right of the Department to respond and provide a copy of the response to the applicant and local government within 45 days of receipt of the application.

(b) The applicant shall provide to the Department a copy of the local government decision on the application for variance within ten days of issuance of the decision.

(c) Any variance granted shall require the applicant to install, operate, and maintain obstruction marking and lighting in compliance with the marking and lighting standards set forth in this rule chapter.

(4) Obstruction Marking and Lighting. Obstruction marking or lighting recommended in an FAA aeronautical determination shall be considered a requirement for the structure for compliance with Department standards. As minimum standards, the Department herein incorporates by reference obstruction marking and lighting standards and guidelines described in the U.S. Department of Transportation, Federal Aviation Administration Advisory Circular 70/7460-1K (AC 70/7460-1K) “Obstruction Marking and Lighting,” dated August 1, 2000. These standards shall be applied as follows:

(a) Objects that exceed an overall height of 200 feet above ground level (AGL), including any appurtenances, or that exceed any federal obstruction standard will be required to be marked or lighted as specifically recommended by the FAA. Marking or lighting of objects lower than 200 feet AGL will be required within specific lateral boundaries of established low level aircraft routes.

(b) Objects which exceed 300 feet AGL up to 500 feet AGL within six nautical miles of a licensed public-use airport or military airfield, shall be marked or lighted in accordance with specific federal obstruction guidelines for those heights. The white lighting required for daytime and twilight, for dual lighting with red/medium intensity white systems, shall be medium intensity. The system includes automatic sensors that change between red and white lighting and also vary the white strobe intensity between twilight and full day.

(c) Objects which exceed 500 feet AGL, within a six nautical mile radius of a public-use airport or military airfield, shall be marked or lighted in accordance with specific federal obstruction guidelines for those heights. The white lighting required for daytime and twilight, for dual lighting with red/high intensity white systems, shall be high intensity.

(d) Objects which exceed 800 feet AGL beyond the six nautical mile radius of public airports or military airfields, shall be marked or lighted in accordance with specific federal obstruction guidelines for those heights. The white lighting required for daytime and twilight, for dual lighting, shall be high intensity.

(e) Specific marking or lighting will not be required if both of the following circumstances exist:

1. The object is masked by surrounding objects marked or lighted under these standards, and

2. The FAA specifically recommends deletion of any marking or lighting because of the masking effect.

(f) When the FAA recommends dual lighting for objects less than the heights specified in this rule chapter because of the need for greater visual conspicuity, the more stringent FAA recommendations shall be required as a condition of the permit issued. Additionally, when an object does not exceed any federal obstruction standard, but because of its particular location, the FAA recommends marking and lighting, the FAA recommendation shall be required as a condition of the permit.

Rulemaking Authority 330.29(4), 333.065, 334.044(2) FS. Law Implemented 330.29, 330.35, 333.025, 333.03(5), 333.07, 333.08 FS. History–New 11-23-72, Amended 4-18-76, 11-19-81, 1-8-85, Formerly 14-60.09, Amended 4-19-89, 12-26-95, 8-5-96, 2-11-97, 10-10-04.