62-600.100 Scope, Intent, Purpose, and Applicability.

(1) Section 403.021(2), Florida Statutes, as amended, the Florida Air and Water Pollution Control Act, established that no wastes are to be discharged to any waters of the state without first being given the degree of treatment necessary to protect the beneficial uses of such water. Toward this end, Sections 403.085 and 403.086, Florida Statutes, set forth requirements for the treatment and reuse or disposal of domestic wastewater. Section 403.051(2)(a), Florida Statutes, requires that any Department planning, design, construction, modification, or operating standards, criteria, and requirements for wastewater facilities be developed as a rule. This chapter is promulgated to implement the provisions and requirements of Sections 120.53(1), 120.55, 403.021, 403.051, 403.061, 403.062, 403.064, 403.085, 403.086, 403.087, 403.088, 403.0881, 403.101, 403.131, 403.161, 403.182, 403.859, and 403.918, Florida Statutes, concerning domestic wastewater facilities.

(2) The requirements of this chapter represent the specific requirements of the Florida Department of Environmental Protection and of Local Pollution Control Programs approved and established pursuant to Section 403.182, Florida Statutes, where such authority has been delegated to those programs. It may be necessary for domestic wastewater facilities to conform with requirements of other agencies, established via interagency agreements (e.g., for mosquito control); the absence of reference to such arrangements in this chapter does not negate the need for compliance with those requirements.

(3) The purpose of Chapter 62-600, F.A.C., is to provide minimum standards for the design of domestic wastewater facilities and to establish minimum treatment and disinfection requirements for the operation of domestic wastewater facilities. All systems shall be designed in accordance with sound engineering practice. Supported by moderating provisions, it is intended that Chapter 62-600, F.A.C., establish a framework whereby design flexibility and sound engineering practice can be used in developing systems with which to manage domestic wastewater in an environmentally sound manner.

(4) As appropriate, Chapter 62-600, F.A.C., shall be used in conjunction with other Department rules relating to the design and operation and maintenance of domestic wastewater facilities.

(5) Standards and requirements in this chapter shall apply only to domestic wastewater treatment, reuse, and disposal facilities (including residuals management facilities).

(a) Standards and requirements shall apply to all new facilities and modifications or expansions of existing facilities that submit complete permit applications to the Department after July 1, 1991.

(b) Standards and requirements shall apply to all existing facilities that submit complete applications for permit renewal after July 1, 1991.

(6) Domestic wastewater facilities that submit complete permit applications on or before July 1, 1991, may:

(a) Continue to comply with the rule requirements that were in effect at the time the permit was issued and with the conditions of the existing construction or operation permit until the expiration of such permit, or

(b) Opt to comply with the requirements of this revised chapter.

(7) The standards and requirements of Part II of Chapter 62-600, F.A.C., and Rules 62-600.500 and 62-600.530, F.A.C., shall be applicable to septic tank drainfield systems and other on-site waste treatment systems with subsurface disposal regulated by this chapter. The reliability requirements of paragraph 62-600.400(1)(b), F.A.C., shall not apply to such septic tank drainfield systems and other on-site waste treatment systems.

(8) The discharge limitation of subsection 62-600.510(4), F.A.C., shall not be applicable to facilities permitted on or before January 1, 1982, that discharge into Class II waters or Class III waters which are subsequently reclassified as Class II waters.

(9) This chapter provides for exemptions, allowances for existing facilities and variations from standards and requirements. Unless specifically provided otherwise, no wastewater permit shall be issued or renewed unless the permit applicant demonstrates that the subject facility is in compliance with the applicable provisions of this chapter.

Specific Authority 403.051, 403.061, 403.062, 403.086, 403.087, 403.088 FS. Law Implemented 403.021, 403.051, 403.061, 403.062, 403.085, 403.086, 403.087, 403.088 FS. History–New 11-27-89, Amended 1-30-91, Formerly 17-600.100, Amended 12-24-96.