62B-33.008 Permit Application Requirements and Procedures.

(1) All applications submitted to the Department or to the appropriate local building department prior to March 1, 2002, the effective date of the Florida Building Code Act (Part VII, Chapter 553, F.S.), shall contain all the information required in subsection 62B-33.008(3), F.A.C.

(2) Applications received by the Department after the effective date of the Florida Building Code Act shall not be required to comply with the provisions of paragraphs 62B-33.008(3)(j), and subsection 62B-33.008(4), F.A.C., except as noted in subsection 62B-33.008(1), F.A.C.

(3) Any person desiring to obtain a permit for construction seaward of the coastal construction control line (CCCL) or 50-foot setback from the Department, except those persons applying pursuant to the emergency procedures in Rule 62B-33.014, F.A.C., shall submit two copies of a completed application form, only one of which is to include the required attachments, to the Bureau at the address below. The permit application form, which is entitled “Application for a Permit for Construction Seaward of the Coastal Construction Control Line or Fifty-Foot Setback” – DEP Form 73-100 (Revised 1/04), is hereby adopted and incorporated by reference. Copies of the form can be obtained by writing the Department of Environmental Protection, Bureau of Beaches and Coastal Systems, 3900 Commonwealth Boulevard, Mail Station 300, Tallahassee, Florida 32399-3000; or by telephoning (850) 487-4475, extension 108. The application shall contain the following specific information:

(a) Name, mailing address, and telephone number of the property owner and of any duly authorized agent making the application on behalf of the owner, and the signature of the applicant.

(b) The name and mailing address of the owners of the immediately adjacent properties, exclusive of street-ends or easements.

(c) Sufficient evidence of ownership including the legal description of the property for which the permit is requested. Sufficient evidence of ownership includes a copy of an executed warranty deed bearing evidence of appropriate recordation; a copy of a long term lease-purchase agreement, or contract for deed; a copy of a property tax receipt bearing the name and address of the current owner; articles of condominium bearing evidence of appropriate recordation (for condominiums); or the cooperative documents defined in Section 719.103(9)(a), F.S. (for residential cooperatives). Other documents submitted as evidence of ownership will be reviewed by the staff and shall be rejected if found not to be sufficient. A copy of a purchase contract or an affidavit from the owner is not sufficient evidence of ownership. If the applicant is not the property owner, the applicant shall submit certification on the form provided by the Department as part of the permit application form, authorizing the applicant to act as the owner’s agent for the purpose of applying for a permit and to act on behalf of the owner in other matters pertaining to the permit.

(d) Written evidence, provided by the appropriate local governmental agency having jurisdiction over the activity, that the proposed activity, that the proposed activity, as submitted to the Bureau, does not contravene local setback requirements or zoning codes and is consistent with the state approved Local Comprehensive Plan.

(e) A statement describing the proposed work, activity, or construction.

(f) Two original copies of a signed and sealed survey of the subject property. The information depicted on the drawing shall be from a field survey conducted not more than six months prior to the date of the application. The survey shall comply with the requirements given in Rule 62B-33.0081, F.A.C.

(g) For major and rigid coastal structures, one copy of a dimensioned site plan drawing to an appropriate scale, on 8 1/2-inch by 11-inch size paper showing the location of the proposed structure(s), the proposed construction limits, and the location and volume of any proposed excavation or fill, and all distances and locations as referenced in subsection 62B-33.0081(1), F.A.C.

(h) For major and rigid coastal structures, one copy of a dimensioned cross-sectional drawing to an appropriate scale, on 8 1/2-inch by 11-inch paper, showing:

1. All subgrade construction or excavation with elevations referenced to the NAVD of 1988.

2. Typical cross-section view of the structural components above grade with elevations for the underside of the building support structure and crest elevations for any proposed coastal or shore protection structure.

3. Location of the control line or, if not established, the MHWL and the 50-foot setback.

4. Typical profile of existing and proposed grade at the site.

5. The location of the contour line corresponding to elevation 0.0 NAVD of 1988.

(i) For structures with proposed permanent exterior lighting, one copy of a dimensioned drawing to an appropriate scale, on 8 1/2-inch by 11-inch paper, showing:

1. The location of all proposed permanent exterior lighting fixtures clearly marked by distinctive symbols for each model used,

2. A table with the column headings shown below providing the specified information for each fixture model used, and

| SYMBOL | FIXTURE (name of stock number) | TOTAL NUMBER OF EACH FIXTURE | BULB WATTAGE AND TYPE (e.g., 40 watt yellow “bug” lamp) | TYPE OF MOUNT (e.g., wall, pole, bollard) | MOUNTING HEIGHT |
| --- | --- | --- | --- | --- | --- |

3. A detailed description or manufacturer’s catalog sheet (cut sheet) for each fixture model used.

(j) Two copies of detailed final construction plans and specifications for all proposed structures or excavation including all planned appurtenant structures, permanent exterior lighting, and utilities. For major structures, these documents shall be signed and sealed by an engineer or architect (as appropriate) licensed in the State of Florida, and the site plan shall include all information required in subsection 62B-33.0081(1), F.A.C.

(k) Two copies of a dimensioned detailed site plan and grading plan, as necessary, to an appropriate scale showing the location of the proposed structure(s) with respect to the CCCL, the location of the proposed construction limits, and the location and volume of any proposed excavation or fill, and all distances and locations as referenced in subsection 62B-33.0081(1), F.A.C. These documents shall be signed and sealed by a design engineer or architect licensed in the State of Florida.

(l) For rigid coastal structures, two copies of detailed final construction plans and specifications for all proposed structures or excavation. These documents shall be signed and sealed by the design engineer licensed in the State of Florida and shall bear the certification specified in paragraph 62B-33.0051(2)(c), F.A.C., and the site plan shall include all information required in subsection 62B-33.0081(1), F.A.C.

(m) Details, including engineering design computations, for any proposed waste or storm water discharge onto, over, under, or across the beach and dune system, such as storm water runoff, swimming pool drainage, well discharge, domestic waste systems, or outfalls.

(n) An anticipated construction schedule.

(o) Two copies of detailed planting plans, including the location of proposed plants, existing native vegetation, and plants to be removed. Plans shall include a plant list with both scientific and common names.

(4) If the application proposes to repair or rebuild, improve, or add an addition to an existing structure, the applicant shall submit a statement from the local governmental agency having jurisdiction over the activity which clearly states whether or not the proposed construction is a substantial improvement as defined in Section 161.54(12), F.S. If a statement is not available, the applicant shall submit to the Department all documentation necessary for the Department to make such a determination. The documentation shall include the cost of the improvement or repair and a figure representing the cumulative total of 50 percent of the market value of the structure, either before the improvement or repair is started or, if the structure has been damaged and is being restored, before the damage occurred.

(5) The staff shall require the applicant to provide other site specific information or calculations as is necessary for proper evaluation of the application. The plans and survey information referenced in this section shall be submitted in Standard Imperial (English) units.

(6) The Department recognizes that the requirements specified in paragraphs 62B-33.008(4)(f), (g), (h), (i), (j), (k), (l), (m), (n), and (o), and Rule 62B-33.0081, F.A.C., may not, due to the project specific circumstances, be applicable or necessary to ensure protection to the beach and dune system. In such cases, the applicant shall, as part of the application, identify those requirements and state the reason why they are inapplicable. The Department shall waive requirements that do no apply.

(7) The applicant shall have 180 days from the date the Department mails a timely request for additional information to submit that information to the Department. If an applicant requires more than 180 days in which to respond to a request for additional information, the applicant may notify the Department in writing of the circumstances, at which time the application shall be held in active status for a period of up to 90 days. Additional extensions shall be granted for good cause shown by the applicant. A showing that the applicant is making a diligent effort to obtain the requested additional information shall constitute good cause. Failure of an applicant to provide the timely requested information by the applicable deadline shall result in denial of the application.

(8) Notwithstanding the provisions under subsection 62B-33.008(7), F.A.C., an applicant whose permit application was received prior to the effective date of the FBC shall have 90 days from the effective date of the FBC in which to submit the information to the Department. If an applicant requires more than 90 days in which to provide the information, the applicant may notify the Department in writing of the circumstances, at which time the application shall be held in active status for one additional period of up to 90 days. No additional extensions shall be granted. Failure of the applicant to provide the timely requested information by the applicable deadline shall result in a denial of the application.

(9) If the Department has received a permit application but has not taken final agency action on it and a major change in coastal conditions occurs which in the determination of the Department renders the information already reviewed insufficient, then the Department shall notify the applicant that they must submit additional information for Departmental review and provide a written waiver of the requirements of Section 120.60, F.S., or the Department shall deny the application.

(10) Permits shall be suspended or revoked in accordance with Rule 62-4.100, F.A.C. In addition, a permit shall be suspended, revoked, or modified by the Department if shoreline changes occurring subsequent to issuance of the permit render the previously authorized activities inconsistent with Chapter 161, F.S., or this rule Chapter 62B-33, F.A.C.

(11) Permits for major structures shall expire three years from the date of issuance unless the Department receives a written request for extension from the applicant demonstrating that the construction phase of the project cannot be completed within three years. In such case, permits for major structures shall expire five years from the date of issuance. Permits for minor structures shall expire one year from the date of issuance. Once a permit has expired, all activity authorized must cease unless a new permit, a time extension pursuant to subsection 62B-33.013(3), F.A.C., or a permit renewal pursuant to subsection 62B-33.013(4), F.A.C., is approved by the Department.

(12) Any substantial modification to a complete application shall require an additional processing fee determined pursuant to subsection 62B-33.0085(4), F.A.C., and shall restart the time requirements of Section 120.60, F.S. For purposes of this rule section, the term “substantial modification” shall mean a modification which is reasonably expected to lead to increased adverse impacts that require a detailed review.

(13) As an alternative to the above procedure, the Department issues field permits for certain minor structures and activities if the Department determines the activity has minor impacts. The field permit form, which is entitled “Field Permit Pursuant to Section 161.053 or 161.052, F.S.”, DEP Form 73-122 (New 5/00), is hereby adopted and incorporated by reference. A copy of the form can be obtained by writing to the Department of Environmental Protection, Bureau of Beaches and Coastal Systems, 3900 Commonwealth Boulevard, Mail Station 300, Tallahassee, Florida 32399-3000, or by telephoning (850) 487-4475, extension 108.

Specific Authority 161.053 FS. Law Implemented 161.052, 161.053 FS. History–New 11-18-80, Amended 7-7-81, 3-17-85, 11-10-85, Formerly 16B-33.08, Amended 8-7-86, Formerly 16B-33.008, Amended 1-26-98, 8-27-00, 12-31-01, 6-13-04.