64E-9.013 Bathing Places.

(1) General – Approval for the development of a public bathing place and a permit to operate a public bathing place shall be obtained from the department.

(2) Development – The following shall be submitted to the department for consideration towards the development of a public bathing place:

(a) Six sets of site plans, prepared by a professional engineer or professional surveyor or mapper which detail the location, contours of the shoreline and bottom, appurtenances such as sanitary facilities, nearby boat docks/mooring facilities, diving or slide facilities, and pertinent details from the sanitary survey. Said professional engineer(s) and surveyors and mappers shall be licensed in the state of Florida under the provision of Chapter 471 or 472, F.S., and shall fulfill the requirements of Section 471.025 or  472.025, F.S.

(b) A sanitary survey identifying potential sources of contamination as exemplified by streams, unsewered residential areas, water and wastewater treatment plants, sewage outfalls, storm drain outfalls, industrial drainage and waste outfalls, agricultural drainage, sanitary landfills, open dumps, animal enclosures, wildlife populations, and potential high erosion areas. The survey shall include consideration of present or possible future pollution of the bathing water from the above potential sources of contamination and from other forms of pollution including bottom deposits, turbidity of water, decaying vegetation, surface runoff, and the anticipated bather load. The survey shall establish that the bathing water has a flow through of a minimum of 500 gallons per anticipated bather per 24 hours, unless the water surface area of the body of water is two acres or more. The bathing load in lakes shall be based on 100 sq. ft. per bather, and only those portions of the lake within the bathing area shall be considered as the basis of the bathing load. Water currents shall not exceed three feet per second. A written report of the sanitary survey shall be submitted to the department and shall include a presentation and evaluation of the findings and a recommendation relative to the development and permitting of the bathing place.

(c) A bacteriological survey shall be submitted to the department and the fecal coliform or enterococci densities indicated by this survey shall not exceed the standards of subsection 64E-9.013(4), F.A.C. The survey shall consist of a minimum of three bacteriological samples collected from the proposed bathing area daily for the first three days of each week for three consecutive weeks. Either MPN or MF counts may be utilized. Should the MF method results differ significantly from the MPN method results, the MPN results shall prevail. The bacteriological survey results shall be reviewed in light of the sanitary survey.

(d) Fees as per Rule 64E-9.015, F.A.C.

(e) A legal survey of the property by a registered land surveyor shall be provided.

(f)  A water clarity measurement by Secchi disk reading in feet using an 8 inch diameter black and white Secchi disk.

(3) Operation.

(a) The following must be submitted prior to operation:

1. Six operating permit applications, DH 917.

2. Fees as per Rule 64E-9.015, F.A.C.

(b) Operational water quality – The water shall be free of chemical and physical substances known or suspected of being capable of creating toxic reactions or skin or membrane irritations. Algae and aquatic vegetation shall be controlled so that no hazard to bathers results.

(c) Bacteriological samples shall be collected monthly. A set of two samples shall be collected for every 200 feet of shoreline, the samples shall be taken a foot below the surface in two feet of water and at least 25 feet apart. The samples shall be analyzed by a certified laboratory and the results submitted to the department. Should the average of these samples exceed 175 fecal coliform per 100 ml, or exceed 28 enterococci per 100 ml, additional sampling shall be required and the results submitted to the county health department.

(d) Inspections – county health departments shall perform two inspections per year which shall include:

1. A site inspection in light of the original sanitary survey.

2. A bacteriological test. The coliform density must not exceed the standards of subsection 64E-9.013(4), F.A.C.

3. A water clarity test shall be performed wherein an 8'' black and white secchi disk shall be visible to a minimum depth of four feet.

(e) Trash and garbage receptacles shall be provided and said trash disposed of at least weekly.

(f) Muck or silt shall not be present from the shoreline to a depth of five feet and aquatic vegetation shall be controlled.

(g) Site specific signage shall be provided. The bathing load shall be posted and due consideration shall be given to safety guidelines such as steep slope, diving areas, deep water, underwater obstruction, or lifeguard not on duty. Additional signage shall be provided if the bathing area is longer than 300 feet.

(h) Restrooms, platforms, diving boards, docks, and walkways shall be kept clean and in good repair. Diving areas shall be readily identified, and shall have adequate water depth for safe diving based on the depth requirements of the FINA standards previously adopted herein. Shallow areas shall not be utilized for diving and shall be so marked.

(i) Glass items and domestic animals are prohibited in the bathing area and on the adjacent beach area.

(j) Sanitary facilities shall be provided and shall be as near to the bathing area as prudent to ensure patron use.

1. Women’s restrooms shall have a fixture set including a water closet and a lavatory.

2. Men’s restrooms shall have a fixture set including a urinal, a water closet and a lavatory.

3. Additional restroom fixture shall be provided based on stated usage. A second water closet, urinal and lavatory shall be provided in the men’s restroom if the stated usage exceeds 50 patrons, but is less than 150 patrons. Another urinal, water closet and lavatory shall be provided for each additional 100 patrons. The number of water closets in the women’s restroom shall be based on a three to two ratio with three water closets being provided in the women’s restroom for every two fixtures in the men’s restroom. For this purpose of establishing the men’s restroom fixture count, both water closets and urinals shall be included. The number of lavatories in the women’s restroom shall match the number in the men’s restroom.

4. Restroom floors shall be impervious, slip resistant and slope to floor drains.

(4) Bacteriological Standards – The enterococci density shall not exceed 61 per 100 ml or the fecal coliform density shall not exceed an average of 200 per 100 ml of sample, nor exceed 400 per 100 ml of sample in 10 percent of the samples, nor exceed 800 per 100 ml of sample in any one day. This average shall be expressed as geometric means.

Specific Authority 381.0011, 381.006, 514.021 FS. Law Implemented 381.0011, 381.0025, 381.006, 386.01, 386.02, 386.03, 386.041, 386.051, 514.021, 514.03, 514.031, 514.04, 514.05, 514.06 FS. History–New 10-5-93, Formerly 10D-5.142, Amended 12-27-98, 5-27-04.