62-18.550  Measurement Sites for New Motor Vehicles.

Sites for measuring sound from new motor vehicles shall meet the following requirements:

(1) Location. The site location shall be a flat open space free of large sound-reflecting surfaces other than the ground (such as signboards, buildings, hillsides, or trees) within 100 feet of the microphone and within 100 feet of the following points on the vehicle path:

(a) The microphone point.

(b) A point 50 feet before the microphone point.

(c) A point 50 feet beyond the microphone point.

(2) Ground Condition. The ground surface of the measuring site shall be smooth asphalt or concrete free of snow, soil, or ashes in at least the triangular area between the microphone and points 50 feet before and beyond the microphone point.

(3) Roadway Surface. The surface of the vehicle path shall be dry and smooth asphalt or concrete pavement free of extraneous material.

Rulemaking Authority 403.061 FS. Law Implemented 403.061, 403.415(5) FS., Chapter 74-110, Laws of Florida. History–New 11-27-74, Formerly 17-18.55, 17-18.550.