# CHAPTER 14-26

# SAFETY REGULATIONS AND PERMIT FEES FOR OVERWEIGHT AND OVERDIMENSIONAL VEHICLES

# 14-26.001	Schedule of Fees for Permits (Repealed)

# 14-26.002	Exemptions from Fee Requirement (Repealed)

# 14-26.003	Purpose (Repealed)

# 14-26.004	Scope (Repealed)

# 14-26.0041	Definitions and Terms

# 14-26.00411	Procedure for Issuance of Permits

# 14-26.0042	Exemption from Permit Requirements

# 14-26.00425	Criteria for Issuance of Permits

# 14-26.0043	Multi-State Travel (Repealed)

# 14-26.00435	Everglades Agricultural Area Tandems

# 14-26.0044	Interstate Movements (Repealed)

# 14-26.005	Intent (Repealed)

# 14-26.0051	Criteria for Issuance of Permits (Transferred)

# 14-26.006	Procedure for Issuance of Road Use Permits (Transferred)

# 14-26.007	Liability of Permittee

# 14-26.008	Schedule of Fees

# 14-26.009	Exemptions from Fee Requirement

# 14-26.0091	Tire Requirements

# 14-26.010	Weight Limitations (Repealed)

# 14-26.011	Waiver of Axle Limitations (Repealed)

# 14-26.012	Movement Conditions and Restrictions

# 14-26.013	Permits to Move Buildings (Repealed)

# 14-26.0131	Permits to Move Ocean-Going Sealed Containerized Cargo Units (Repealed)

# 14-26.01311	Permits to Move Sealed Containerized Loads

# 14-26.014	Non-Compliance

# 14-26.015	Penalties

## 14-26.001 Schedule of Fees for Permits.

Rulemaking Authority 316.550 FS. Law Implemented 316.550 FS. History–New 12-1-63, Amended 6-20-65, 5-23-68, 10-13-72, 10-30-78, Formerly 14-26.01, Repealed 8-26-82.

## 14-26.002 Exemptions from Fee Requirement.

Rulemaking Authority 316.550 FS. Law Implemented 316.550 FS. History–New 10-13-72, Amended 10-30-78, Formerly 14-26.02, Repealed 8-26-82.

## 14-26.003 Purpose.

Rulemaking Authority 316.550, 334.044(2) FS. Law Implemented 316.515, 316.550 FS. History–New 8-26-82, Formerly 14-26.03, Amended 9-15-87, Repealed 6-23-96.

## 14-26.004 Scope.

Rulemaking Authority 316.550, 334.044(2) FS. Law Implemented 316.515, 316.550 FS. History–New 8-26-82, Formerly 14-26.04, Amended 9-15-87, Repealed 6-23-96.

## 14-26.0041 Definitions and Terms.

All terms in this rule chapter shall have the same meaning as defined in section 316.003, F.S., except that “Department” shall refer to the Department of Transportation. Additionally, the following terms are defined:

(1) “Applicant” means a person or entity requesting a permit.

(2) “Axle Spacing” means the measurement between the centers of the axles as measured from center-to-center of wheel hubs.

(3) “Divisible Load” means a load which exceeds the legal weight, length, width or height limits established in sections 316.515 and 316.535, F.S., which can be dismantled using appropriate equipment without destroying the value or compromising the intended use of the load.

(4) “Escort” means a person authorized in the manner prescribed in paragraphs 14-26.012(2)(b)-(c), F.A.C., to perform accompanying duties for overweight or overdimensional vehicles.

(5) “Escort Vehicles” means a vehicle independent of the permitted vehicle, equipped with a working, amber warning light located on top of the escort vehicle, and operated by a qualified escort, law enforcement escort, or any combination shown in Rule 14-26.012, F.A.C.

(6) “Excluding Holidays” means movement is prohibited all day on New Year’s Day, Memorial Day, Independence Day, Labor Day, Thanksgiving, the day after Thanksgiving, and Christmas. If any of these holidays fall on Saturday, the preceding Friday shall also be observed as a holiday. If any of these holidays fall on a Sunday, the following Monday shall also be observed as a holiday.

(7) “External Bridge” or “outer bridge” means the distance from the center of the front steering axle of the vehicle (or combination of vehicles) to the center of the last axle of the vehicle (or combination of vehicles).

(8) “Fifth Wheel” means a device mounted on a truck tractor or similar towing vehicle (e.g., converter dolly) which interfaces with and couples to the upper coupler assembly of a semitrailer.

(9) “Flag” means a red or florescent orange device used to warn approaching traffic of a safety hazard.

(10) “Governmental Entity” means as defined in section 215.985(2)(c), F.S.

(11) “Inner-Bridge” means the distance between the centers of any two or more consecutive axles on a vehicle (or combination of vehicles) traveling on the interstate system only, exclusive of the external bridge.

(12) “Kingpin Setting” means the distance between the kingpin or other peg which locks into the fifth wheel and the center of the rear axle or the center of the rear axle grouping (whichever applies).

(13) “Law Enforcement Escort” means any police officer as defined in section 316.003(32), F.S., operating any vehicle owned by a law enforcement agency using blue or red and blue warning lights to accompany an oversize/overweight vehicle.

(14) “Local Moves” means hauling not more than a 50 mile radius from the point of origin.

(15) “Manufactured Building” or “modular building” means a closed structure, building assembly, or system of subassemblies, which may include structural, electrical, plumbing, heating, ventilating, or other service systems made for installation or erection as a finished building or part of a finished building, which shall include, but not be limited to residential, commercial, institutional, storage, and industrial structures. The term includes buildings not intended for human habitation such as lawn storage buildings and storage sheds made and assembled offsite by a manufacturer certified in conformance with section 553.381, F.S.

(16) “Manufactured Home” means as defined in section 320.01(2)(b), F.S.

(17) “Mobile Home” means as defined in section 320.01(2)(a), F.S.

(18) “Multiple Loading” means the placing of more than one item on a vehicle so as to cause the overall measurements to exceed the maximum length, width, height, and weight limitations established in sections 316.515 and 316.535, F.S.

(19) “Multi-Trip Permit” or “blanket” or “annual permit” or “Route Specific Blanket Permit” means authorization issued to allow multiple trips for a period not to exceed 12 months.

(20) “Non-Routine Permit” means authorization issued with a structural evaluation or override authorization.

(21) “Overdimensional” or “oversize” means any vehicle configuration, including the load, which exceeds the limitations provided in Section 316.515, F.S.

(22) “Overhang” means that portion of a load or vehicle attachment that projects beyond the front or rear wheels of a vehicle or the front or rear bumper of a vehicle if it is equipped with a front or rear bumper.

(23) “Overweight” means any vehicle configuration, including the load, which exceeds the limitations provided in Section 316.535, F.S.

(24) “Permit Office” means the Permit Section of the Office of Maintenance, Florida Department of Transportation, with offices located in Tallahassee, Florida. Website: www.fdotmaint.com/permit/.

(25) “Permittee” means the applicant to whom an oversize/overweight permit is issued.

(26) “Routine Permit” means authorization issued by the Department for an overweight or overdimensional load that did not require a structural evaluation, local movement restrictions, or override authorization.

(27) “Self-Propelled Equipment” means a single rigid frame unit propelled with its own power source which does not transport a divisible load, and includes equipment such as earth handling equipment, cranes (which may include a dolly attachment), derricks and fire trucks.

(28) “Trip Permit” means authorization issued to allow a single hauling of a load from point of origin to destination.

(29) “Truck Crane” means any vehicle (which may include a dolly attachment) designed and constructed to be used primarily for lifting, lowering, or traversing while operating from either a secure stationary position, or in a rolling position, if specifically designed for rolling operation.

(30) “Valid Permit” means authorization pursuant to section 316.550, F.S., by the Department that has not been altered, changed, or otherwise modified, unless in writing by the Department, accompanied by the original permit.

(31) “Warning Light” means a class 2 electrical lighting device located on a permitted vehicle and/or escort vehicles, used to warn all approaching traffic of a possible safety hazard. The device shall be any one or combination of the following:

(a) Rotating;

(b) Strobe;

(c) Flashing.

(32) “Warning Sign” means a sign device, located on permitted vehicle and escort vehicles, used to warn all approaching traffic of a possible safety hazard.

(33) “Wrecker Permit” means authorization issued for the operation of a wrecker where the combined weight of the wrecker plus towed disabled vehicle exceeds the maximum weight established by section 316.535, F.S.

Rulemaking Authority 316.550(6), 334.044(2) FS. Law Implemented 316.515, 316.550 FS. History–New 9-15-87, Amended 7-21-91, 6-23-96, 11-10-98, 2-1-10, 10-4-10, 2-5-13, 8-23-16, 4-24-18.

## 14-26.00411 Procedure for Issuance of Permits.

(1) Purpose. The purpose of this rule chapter is to protect the public safety, to reduce interference with traffic flow on state owned highways and structures, and to preserve the state’s transportation facilities by providing standards and procedures to govern issuance of permits for overweight and overdimensional vehicles and loads operating over state owned roadways and structures. Travel authorization and/or permits for travel on local roadways must be obtained from local authorities. The rules of this rule chapter apply to all persons or entities operating overweight and overdimensional vehicles and loads over state maintained roads, which are not specifically exempt under Chapter 316, F.S.

(2) Intent. It is the intent of the Department to require that all reasonable steps be taken to reduce the vehicle load to legal limits of weight and dimensions. Permits for overweight and overdimensional vehicles and loads are intended for a single item load which cannot reasonably be dismantled or disassembled and which cannot reasonably be shipped by rail, water, or air.

(3) Administration. The administration of these rules is assigned to the Department’s Permit Office, located in Tallahassee, Florida, whose mailing address is:

Florida Department of Transportation

Permit Section

605 Suwannee Street, MS #62

Tallahassee, Florida 32399-0450

(4) Permitting Process. Payment for permits shall be in cash, by cashier’s check, personal or company check, money order, or credit card. Permit requests must be received at least ten business days before scheduled movement for non-routine permits. The applicant must complete all fields on Form 850-040-02, Request for Special Road Use Oversize/Overweight Permit Application rev. 6/16 incorporated herein at https://www.flrules.org/Gateway/reference.asp?No=Ref-07283, or complete an online Application at www.fdotmaint.com/permit, and provide the following:

(a) Total gross weight of vehicle/vehicle combination to include permitted load if over legal weight. Otherwise, the applicant must state that the gross weight is legal.

(b) External bridge and individual axle spacings of vehicle/vehicle combination (center of hub to center of hub) if over legal weight.

(c) Total number of axles and total weight on each axle of vehicle/vehicle combination if over legal weight. Otherwise, the applicant must state that the axle weights are legal.

(d) Total width of vehicle and/or load at widest point.

(e) Total length of the vehicle/vehicle combination and/or load from front to rear to include front and rear overhang. If there is any overhang, separate measurements are to be provided in addition to the total length.

(f) Total height of the vehicle and/or load from the pavement to the highest point of the vehicle and/or load.

(g) Description of load to be transported.

(h) Requested route of travel containing detailed information including origin, destination, physical addresses, mile markers, or intersections. This applies to trip permit applications only.

(5) The Department is responsible for verifying the load carrying capacity of the route (bridges and similar load bearing structures). The applicant is responsible for verifying adequate vertical (height) and horizontal (length and width) clearances exist on route. No movement shall be made under any permit until the route has been surveyed to verify that the route can accommodate the vehicle and load. A survey letter must be maintained with the load during movement and produced to law enforcement and weight inspectors upon request. The survey letter must be on the hauler’s letterhead and include a signed statement verifying that the route has been surveyed, and that clearances exceed the requested permitted dimension by a minimum of 6 inches for height greater than 15 feet and 2 feet on each side for width greater than 16 feet. The surveyed route and the route shown on the permit must match. Surveying a route prior to movement of the load does not exempt the hauler from being required to obtain a permit prior to any movement. In addition, applications for permits for vehicles and loads with a height greater than 18 feet and/or width greater than 22 feet shall be supported by a survey letter from the hauler.

(6) Structural Evaluation. In addition to the information required for issuance of a permit, a schematic of the vehicle showing all longitudinal and transverse spacings, axle weights and dimensions must be provided at least ten business days before a proposed move when any axle exceeds 30,000 pounds, or when the vehicle’s gross weight is 300,000 pounds or more. Applicants, whose vehicles gross vehicle weight is less than 300,000 pounds, will be required to provide a schematic as well when an Engineer of the Office of Maintenance, Bridge Section, determines that a structural analysis is needed.

Rulemaking Authority 316.550, 334.044(2) FS. Law Implemented 316.515, 316.535, 316.550 FS. History–New 8-26-82, Formerly 14-26.06, Amended 9-15-87, 7-21-91, 6-23-96, 11-10-98, Formerly 14-26.006, Amended 2-1-10, 10-4-10, 2-5-13, 8-23-16, 3-9-17, 4-24-18.

## 14-26.0042 Exemption from Permit Requirements.

Certain dimensional (width, height, length) exemptions from permit are enumerated in sections 316.515 and 316.535, F.S. Exempted entities are also exempt from the requirements for qualified escorts. No permit exemptions are allowed for weight.

Rulemaking Authority 316.550, 334.044(2), 316.535 FS. Law Implemented 316.515(5)(a), 316.535(6) FS. History–New 9-15-87, Amended 7-21-91, 4-19-94, 6-23-96, 11-10-98, 2-1-10.

## 14-26.00425 Criteria for Issuance of Permits.

(1) The Department shall consider the following criteria when evaluating permit requests and prescribing conditions limiting the use of said permit:

(a) Whether the load can be reasonably dismantled or disassembled;

(b) Protection of the motoring public from traffic hazards created by the movement of overweight and overdimensional vehicles or loads on state owned highways and structures;

(c) Prevention of undue delays in the normal flow of traffic;

(d) Prevention of damage to the highway pavement, facilities, and structures;

(e) Assistance needed for transportation problems involving excess size or weight;

(f) Whether vehicle(s) meet the Department’s established axle load and axle spacing requirements based upon structural analysis of the bridge structures to be crossed;

(g) Temporary conditions such as construction;

(h) The applicant’s survey letter indicating available vertical clearance on the proposed route for all loads/vehicles over 18 feet high;

(i) The applicant’s survey letter indicating available horizontal clearance on the proposed route for all loads/vehicles over 22 feet wide;

(j) The applicant’s previous permit compliance history;

(k) Other items which affect traffic flow or safety;

(l) All details relevant to the proposed move as presented by the applicant and as requested by the Department.

(2) Override Authority.

(a) Pursuant to section 316.550, F.S., the Department may issue permits for vehicles or loads not specifically authorized by statute or rule, thereby exceeding the limitations of sections 316.515 and 316.535, F.S., and Rule Chapter 14-26, F.A.C.

(b) To obtain a permit for vehicles, loads, or travel not authorized in this rule chapter, an applicant must include, with the permit application, a letter of essentiality from a government entity or the ultimate recipient of an essential service. The letter of essentiality must include a justification for granting override authority. A letter from the hauler, distributor, or manufacturer will not be accepted. The letter must verify that the load has been reduced to the smallest size possible, cannot reasonably be shipped by any other means of transportation, and state why the move is essential in the interest of public safety, national defense or other extenuating circumstances.

(c) The applications, supporting documentation, authorizations, and permits will be documented and maintained by the Department.

(d) Emergencies. Upon a Governor’s Declaration of Emergency, in order to allow response to the emergency, and after safety considerations, the Department may temporarily relieve vehicles of certain permit restrictions by issuing an emergency permit letter.

Rulemaking Authority 316.550, 334.044(2) FS. Law Implemented 316.515, 316.550, 316.565, 334.044(27) FS. History–New 9-15-87, Amended 6-23-96, 11-10-98, Formerly 14-26.0051, Amended 2-1-10, 2-5-13, 8-23-16.

## 14-26.0043 Multi-State Travel.

Rulemaking Authority 316.550 FS. Law Implemented 316.550, 320.0104(2) FS. History–New 11-22-94, Amended 2-1-10, Repealed 8-23-16.

## 14-26.00435 Everglades Agricultural Area Tandems.

Everglades Agricultural Area tandems comprised of any combination of truck tractor, as defined in Section 316.003(100), F.S., semitrailer, as defined in Section 316.003(75), F.S., and trailer, as defined in Section 316.003(96), F.S., coupled together so as to operate as a single unit in which the semitrailer and the trailer unit are each between 28 and 48 feet in length, being used for the primary purpose of transporting farm products, as defined in Section 823.14(3)(c), F.S., will be permitted to operate within the Everglades Agricultural Area as described in Section 373.4592(15), F.S., and identified in the Everglades Agricultural Area Map incorporated herein at: http://www.flrules.org/Gateway/reference.asp?No=Ref-12097, subject to the provisions of this rule chapter and the following requirements:

(1) Permit.

(a) A Request for Special Road Use Oversize/Overweight Permit Application must be submitted in accordance with subsection 14-26.00411(4), F.A.C., for a Route Specific Multi-Trip Blanket Permit.

(b) Permits are not renewed. An application, which is subject to review and approval, must be submitted every 3 months for new permits.

(c) The permit must be maintained in the truck tractor at all times during tandem operation and provided to the Florida Highway Patrol or any other local law enforcement agency upon request.

(d) Only truck tractor, semi-trailer, and trailer combinations are allowed.

(2) Designated Route.

(a) Travel is limited to within the identified Everglades Agricultural Area, not to exceed a radius of 60 miles of the loading point.

(b) The applicant must specify the route that will be used and include an analysis of the route conducted by a Professional Engineer licensed in the State of Florida, which analysis must be signed and sealed.

(c) The analysis must include a:

1. Diagram of the route.

2. Vehicle configuration.

3. Verification that horizontal and longitudinal clearances exist.

4. Route Analysis must show access on public roads and streets that have not been restricted from tandem trailer truck operations in accordance with Section 316.515, F.S.

5. Route Analysis must include determination of safe and unimpeded operations at all route intersections (Signalized and Unsignalized).

6. Everglades Agricultural Area tandems must meet the Minimum Turning Path for Double-Trailer Combination (WB-109D) as defined by American Association of State Highway and Transportation Officials (AASHTO) Design Vehicle Standards and contained in AASHTO’s A Policy on Geometric Design of Highways and Streets (Green Book). AASHTO’s A Policy on Geometric Design of Highways and Streets, 7th Edition (2018), is hereby incorporated by reference and made part of this rule. A copy of the Green Book may be ordered from the AASHTO Bookstore website: https://bookstore.transportation.org. A copy is available for public inspection during regular business hours at the Florida Department of Transportation, Office of Maintenance, 605 Suwannee Street, Tallahassee, Florida 32399, (850)410-5530 and at the Florida Department of State, Administrative Code and Register Section, Room 701, the Capitol, Tallahassee, Florida 32399, (850)245-6270. Posting of the preceding material on the internet for purposes of public examination would violate federal copyright law.

7. Everglades Agricultural Area tandems shall not use intersection turning lanes along the route that are shown to be less than the total length of the combined transport unit.

8. The analysis must be signed and sealed by a Professional Engineer, certifying that the route can safely accommodate the vehicle configuration for both length (state and local network) and weight (local bridges only).

(d) For travel on local roadways, the applicant must submit a letter or other documentation from the local entity having jurisdiction over the roadway authorizing travel on the roadway.

(3) Prohibited routes.

(a) No travel, except for direct crossing over, is permitted on roadways on the National Network as found in 23 CFR Part 658. 23 CRF Part 658 is hereby incorporated by reference http://www.flrules.org/Gateway/reference.asp?No=Ref-12426 and made part of this rule, and is available electronically at https://www.fhwa.dot.gov/legsregs/directives/fapg/cfr0658b.htm.

(b) Routes will not include local roadways that prohibit truck traffic.

(c) No daytime travel will be permitted within designated school zones.

(4) Driver Requirements.

(a) All drivers of Everglades Agricultural Area tandems must comply with the regulations in accordance with Section 316.302, F.S., unless specifically excluded under provisions of the Florida Uniform Traffic Control Law, Chapter 316, F.S.

(b) All drivers of Everglades Agricultural Area tandems must have a current Commercial Driver’s License (CDL) with an endorsement for double trailers consistent with the provisions of Section 322.57, F.S.

(c) Due to the experience needed and the difficulty handling Everglades Agricultural Area tandems, the driver exemptions for farm vehicle drivers provided in Sections 316.302(2), (3), F.S., shall not apply to drivers of Everglades Agricultural Area tandems.

(d) All drivers of Everglades Agricultural Area tandems must be properly trained and certified to operate a Longer Combination Vehicle in accordance with 49 CFR Parts 380 and 391. 49 CFR Parts 380 and 391 are hereby incorporated by reference http://www.flrules.org/Gateway/reference.asp?No=Ref-12427, http://www.flrules.org/Gateway/reference.asp?No=Ref-12428 and made part of this rule. 49 CFR Part 380 is available electronically at https://www.govinfo.gov/content/pkg/CFR-2019-title49-vol5/xml/CFR-2019-title49-vol5-part380.xml. 49 CFR Part 391 is available electronically at https://www.govinfo.gov/content/pkg/CFR-2011-title49-vol5/xml/CFR-2011-title49-vol5-part391.xml.

(e) All drivers of Everglades Agricultural Area tandems must have a minimum of five years of experience driving truck tractor, semi-trailer, and trailer combinations.

(f) A driver of an Everglades Agricultural Area tandem must have had no suspension or revocation of driving privileges in any state or province during the past three years where such suspension arose out of operations of a commercial motor vehicle.

(5) Overall Length, Height, and Width.

(a) The overall cargo carrying length of Everglades Agricultural Area tandems measured from the front of the first trailer to the rear of the second trailer, including the interval between the two trailers, shall not exceed 106 feet.

(b) The Everglades Agricultural Area tandems shall not exceed 13 feet 6 inches in height or 8 feet 6 inches in width.

(6) Weight and Axle Requirements.

(a) All overweight rules of Section 316.535, F.S., shall apply to Everglades Agricultural Area tandems unless specifically excluded under the provisions of this rule chapter.

(b)The maximum weight on any axle shall not exceed 22,000 pounds.

(c) The maximum gross weight of the truck tractor and first trailer shall not exceed 88,000 pounds.

(d) The maximum gross weight of the dolly and second trailer shall not exceed the lesser of:

1. 67,000 pounds, or

2. The weight provisions of the State’s outer bridge formula set forth in Section 316.535(5), F.S., as measured between the center of the foremost axle of the dolly and the rearmost axle of the second trailer.

(e) Maximum gross weight shall not exceed 155,000 pounds.

(f) A minimum of five load bearing axles are required unless stated otherwise in a valid Everglades Agricultural Area tandem permit issued by the Department.

(g) The applicant must identify the total number of axles, the distance between each axle, and total weight on each axle as part of the application.

(7) Truck Tractor Requirements.

(a) A truck tractor used to haul trailers in an Everglades Agricultural Area tandem trailer configuration shall be capable of hauling the maximum gross weight authorized by the permit.

(b) A vehicle that has been placed out-of-service based upon an inspection of the vehicle pursuant to Section 316.302, F.S., will have its permit suspended or revoked, in accordance with subparagraph 14-26.014(1)(a)1., F.A.C., until the out-of-service condition is corrected.

(8) Brake Requirements.

(a) Every Everglades Agricultural Area tandem shall be equipped with full air brakes on the tractor and air brakes on the dolly and trailers. All brakes shall equal or comply with both the equipment requirements and the performance standards cited in Chapter 316, F.S.

(b) The brakes on any vehicle or combination of vehicles, used in Everglades Agricultural Area tandem operations shall be adequate to control the movement of, and to stop and hold, such vehicle, or combination of vehicles, and meet the requirements of the provisions of the Florida Uniform Traffic Control Law, Chapter 316, F.S., and Section 316.262, F.S.

(9) Converter Dolly Requirements.

(a) A converter (fifth-wheel) dolly used in Everglades Agricultural Area tandem operations may have either a single or a double axle, according to its total gross weight. In addition to the tow bar(s), the dolly vehicle must be equipped with safety chains or cables for connecting the dolly to the trailer and adequate to prevent breakaway.

(b) When the distance between the rear of the first trailer and the front of the second trailer is 10 feet or more, the dolly shall be equipped with a device, or the trailers shall be connected along the sides with suitable material to alert other motorists that the trailers are connected and are in effect one unit.

(10) Inspection by Driver.

(a) After all the component vehicles in an Everglades Agricultural Area tandem combination are completely hooked up and prior to the departure of the unit from the assembly area, the driver or a mechanic shall inspect the tandem unit to ensure that each item is in proper operating condition.

(11) Coupling Devices/Hitch Connections.

(a) Vehicles in an Everglades Agricultural Area tandem combination shall be designed, constructed, and connected as to ensure that shifting or swerving from side to side will not exceed two inches to each side of the path of the towing vehicle when it is moving in a straight line.

(b) All coupling devices/hitch connections shall be of a no-slack type which must be visible and operating. All drawbars, pickup plates, and fifth wheels must be rated to exceed the weight carried. Any kingpin must be rated to exceed the weight carried. Any kingpin must be solid and must be permanently fastened.

(12) Operations under Hazardous Conditions.

(a) Drivers of Everglades Agricultural Area tandems shall exercise extreme caution and reduce speed when hazardous conditions exist, such as fog, smoke, dust, mist, or rain.

(b) The Florida Highway Patrol, or any other local law enforcement agency, may restrict or prohibit operations during periods when traffic, weather, or other safety conditions make such operations unsafe or inadvisable.

(13) Permittee Responsibility.

(a) The permittee is responsible for any vehicle operating with an Everglades Agricultural Area tandem permit and other certifications and for complete compliance with all terms of the permit and certification, including:

1. Ensuring that the driver is qualified to operate the vehicle and understands the terms and conditions of the permit, certifications, and the provisions of this rule chapter;

2. Ensuring that the vehicle is inspected and maintained in a safe and reliable condition; including ensuring all commercial motor vehicles used in Everglades Agricultural Area tandem combinations are annually inspected in accordance with 49 CFR Part 396. 49 CFR Part 396 is hereby incorporated by reference http://www.flrules.org/Gateway/reference.asp?No=Ref-12429, made part of this rule, and is available electronically at https://www.govinfo.gov/content/pkg/CFR-2011-title49-vol5/xml/CFR-2011-title49-vol5-part396.xml;

3. Ensuring that the vehicle operates in conformity with the permit, certifications, and the provisions of this rule chapter;

4. Ensuring all documentation, including the permit, the analysis of the designated route, and the authorization letter from the local entity, if applicable, is maintained and available for review when requested by law enforcement; and

5. Ensuring that the driver has proof of training/certification, for Longer Combination Vehicles, to be presented to law enforcement if vehicle is stopped for inspection.

(14) Sunset.

The provisions of this rule chapter shall automatically expire on January 1, 2025, unless the Everglades Agricultural Area tandems permitting program is reauthorized by the Legislature in accordance with Section 316.5501(2), F.S.

Rulemaking Authority 316.550(6), 334.044(2) FS. Law Implemented 316.302, 316.515, 316.535, 316.550, 316.5501 FS. History‒New 12-13-20.

## 14-26.0044 Interstate Movements.

Rulemaking Authority 316.550 FS. Law Implemented 316.550, 320.0104(2) FS. History–New 3-28-95, Repealed 2-1-10.

## 14-26.005 Intent.

Rulemaking Authority 316.550, 334.044(2) FS. Law Implemented 316.515, 316.550 FS. History–New 8-26-82, Formerly 14-26.05, Amended 9-15-87, Repealed 6-23-96.

## 14-26.0051 Criteria for Issuance of Permits.

Rulemaking Authority 316.550, 334.044(2) FS. Law Implemented 316.515, 316.550, 334.044(27) FS. History–New 9-15-87, Amended 6-23-96, 11-10-98, Transferred to 14-26.00425.

## 14-26.006 Procedure for Issuance of Road Use Permits.

Rulemaking Authority 316.550, 334.044(2) FS. Law Implemented 316.550 FS. History–New 8-26-82, Formerly 14-26.06, Amended 9-15-87, 7-21-91, 6-23-96, 11-10-98, Transferred to 14-26.00411.

## 14-26.007 Liability of Permittee.

Permits are granted with the specific understanding that the permittee shall be responsible and liable for any damage to state roadways and structures. The permittee shall hold blameless and harmless and shall indemnify the State of Florida, Department of Transportation and members thereof, its officers, agents and employees against any and all claims, demands, loss, injury, damage, actions and costs of actions whatsoever, which they or any of them may sustain by reason of any and all acts of omission or commission arising in any manner out of the issuance of the permit or the operation of the vehicle, load, or escort and load.

(1) In order to obtain a permit to operate a vehicle or combination of vehicles and load in excess of the legal height, length, width, or weight limitations of section 316.515 or 316.535, F.S., the permittee will be required to have one of the following:

(a) Insurance in the amount of $100,000 per person and $200,000 per accident or occurrence for property damage; or.

(b) A bond in the amount of $100,000 per person and $200,000 per accident or occurrence made payable to State of Florida.

(2) Permittees obtaining and operating a commercial motor vehicle as defined in section 207.002(2), F.S., shall be required to comply with the minimum insurance requirements of section 627.7415, F.S.

Rulemaking Authority 316.550, 334.044(2) FS. Law Implemented 316.535, 316.550, 316.560 FS. History–New 8-26-82, Formerly 14-26.07, Amended 9-15-87, Repromulgated 4-22-92, Amended 6-23-96, 2-1-10.

## 14-26.008 Schedule of Fees.

The following schedule of fees shall be charged by the Department for permits for overweight and/or overdimensional vehicles operating on state owned roadways and bridges:

| TABLE 1A – SCHEDULE OF FEES FOR OVERDIMENSION PERMITS |
| --- |
|  | TRIP PERMIT 10 Days | MULTI-TRIP PERMITS 12 Months | ROUTE SPECIFIC MULTI-TRIP PERMIT 3 Months |
| (1) OVERDIMENSION |  |
| (a) Straight trucks and semi-truck-tractor-trailer. |  |  |  |
| Up to 12 feet wide, or up to 13 feet 6 inches high or up to 85 feet long. | $5.00 | $20.00 | $5.00 |
| Up to 14 feet wide or up to 14 feet 6 inches high or up to 95 feet long. | $15.00 | $150.00 | $38.00 |
| Up to 14 feet wide or up to 18 feet high or up to 120 feet long. | $25.00 | $250.00 | $63.00 |
| Over 14 feet wide or over 18 feet high or over 120 feet long. | $25.00 | NOT ISSUED | $125.00 |
| (b) Overlength semi-trailers of legal width, height, and weight, which exceed 53 feet In Length up to 57 feet 6 inches in length or overlength semi-trailer with kingpin setting greater than 41 feet. | $10.00 | $30.00 | NOT ISSUED |
| (c) Truck crane or earth handling equipment moving under own power, up to 12 feet wide or 14 feet 6 inches high. | $15.00 | $150.00 | $38.00 |
| *(d) Trailers or equipment towed with ball or pintle. |  |  |  |
| *Up to 10 feet wide or up to 13 feet 6 inches high or up to 80 feet long. | $5.00 | $20.00 | $5.00 |
| *Up to 12 feet wide or up to 13 feet 6 inches high or up to 105 feet long. | $5.00 | $330.00 | $83.00 |
| *Up to 14 feet wide or up to 14 feet 6 inches high or up to 105 feet long. | $15.00 | $500.00 | $125.00 |
| Over 14 feet wide or over 14 feet 6 inches high or over 105 feet long. | $25.00 | NOT ISSUED | $250.00 |
| NOTE: All permitted dimensions (length, height, width) must be within limits shown for permit fee. |

| TABLE 1B – SCHEDULE OF FEES FOR OVERWEIGHT VEHICLES |  |
| --- | --- |
|  | TRIP PERMIT 10 Days | MULTI-TRIP PERMITS 12 Months | ROUTE SPECIFIC MULTI-TRIP PERMITS 3 months |
| (2) OVERWEIGHT |  |
| *(a) Up to 95,000 pounds. | $0.27 Per Mile | **$240.00 | $60.00 |
| *(b) Up to 112,000 pounds. | $0.32 Per Mile | **$280.00 | $70.00 |
| *(c) Up to 122,000 pounds. | $0.36 Per Mile | **$310.00 | $78.00 |
| *(d) Up to 132,000 pounds. | $0.38 Per Mile | **$330.00 | $83.00 |
| *(e) Up to 142,000 pounds. | $0.42 Per Mile | **$360.00 | $90.00 |
| *(f) Up to 152,000 pounds. | $0.45 Per Mile | **$380.00 | $95.00 |
| *(g) Up to 162,000 pounds. | $0.47 Per Mile | **$400.00 | $100.00 |
| (h) Up to 199,000 pounds. | $0.003 Per 1,000 Pounds Per Mile | $500.00 | $125.00 |
| (i) Over 199,000 pounds. | $0.003 Per 1,000 Pounds Per Mile | NOT ISSUED | $250.00 |
| (j) Containerized Cargo Unit. | $0.27 Per Mile | $500.00 | $125.00 |
| (k) Overall Wheel Base (Inner Bridge/External Bridge). | $10.00 | $35.00 | NOT ISSUED |
| (l) Implements of husbandry, farm equipment, agricultural trailers/products and forestry equipment (Local Moves Only). | $5.00 | $17.00 | NOT ISSUED |
| (3) SPECIAL PERMIT FEES |  |
| Transmission Fee | $5.00 | NOT APPLICABLE | NOT APPLICABLE |
| *Dimensions greater than 12 feet wide or 13 feet 6 inches high or 85 feet long will have an additonal dimension fee with a combined fee of not to exceed $500.00. NOTE: For weights over 80,000 pounds [paragraphs (2)(a) through (h), above], add an administrative cost of $3.33 for issuance of permit, which does not include the costs charged by wire services for their services. Permit fees shall be based on 25 mile increments rounded up to the nearest dollar. Example: A 112,000 pound load traveling 67.5 miles would cost (75 miles X $0.32) plus $3.33 = $27.33 rounded up to $28.00 in addition to the $5.00 transmission fee when applicable. |

Rulemaking Authority 316.550, 334.044(2) FS. Law Implemented 316.550 FS. History–New 8-26-82, Formerly 14-26.01, Amended 12-6-83, Formerly 14-26.08, Amended 9-15-87, 7-21-91, 4-22-92, 3-1-94, 6-23-96, 11-10-98, 2-1-10, 10-4-10, 2-5-13, 8-23-16, 4-24-18.

## 14-26.009 Exemptions from Fee Requirement.

The following entities are exempt from the fee requirements specified in Rule 14-26.008, F.A.C., above:

(1) Governmental Entities.

(2) Special taxing districts.

(3) Seminole Tribe as defined in Chapter 285, F.S.

(4) Any person or entity moving portable public school buildings.

(5) Implement of husbandry, farm equipment, agricultural trailers and forestry equipment (oversize only) as provided in section 316.515(5), F.S.

(6) Movement of loads in response to a Governor’s Declaration of Emergency.

These vehicles must obtain an overweight and/or overdimensional permit to operate on state owned roadways.

Rulemaking Authority 316.550 FS. Law Implemented 316.550, 316.565 FS. History–New 8-26-82, Formerly 14-26.09, Amended 6-23-96, 11-10-98, 2-1-10, 10-4-10, 2-5-13.

## 14-26.0091 Tire Requirements.

(1) Each axle must have tires of the same size and construction. Tires must be properly inflated for the load to be carried. In no event shall any tire, wheel or rim exceed the manufacturer’s maximum load-carrying limit. Tires and tire usage must be consistent with the requirements of 49 C.F.R., Section 393.75, rev. 10/08, as required by section 316.302(1), F.S.

(2) A vehicle equipped with dual tires may have the dual tires replaced by a single tire so long as the vehicle, axle, and tire load ratings are not exceeded.

(3) No tire may exceed 550 pounds per inch of tire section width (plus scale tolerance) as defined by the rating molded in the tire sidewall. For example, a designation of 445/50R22.5 designates a tire section width of 445 mm (17.5 inches).

Rulemaking Authority 316.302(1), 334.044(2) FS. Law Implemented 316.302(1), 316.535(6) FS. History–New 2-1-10, Amended 2-5-13.

## 14-26.010 Weight Limitations.

Rulemaking Authority 316.550 FS. Law Implemented 316.550 FS. History–New 8-26-82, Amended 12-6-83, Formerly 14-26.10, Amended 4-22-92, 6-23-96, 11-10-98, Repealed 10-4-10.

## 14-26.011 Waiver of Axle Limitations.

Rulemaking Authority 316.550 FS. Law Implemented 316.550 FS. History–New 8-26-82, Amended 12-6-83, Formerly 14-26.11, Amended 11-10-98, Repealed 2-1-10.

## 14-26.012 Movement Conditions and Restrictions.

(1) Operational use of permits. The configuration and weight(s) of a vehicle and its load traveling under permit must match the configuration and weight(s) described on the permit and any authorized amendments to that permit. For vehicles traveling under a trip permit, the vehicle or load must match either the truck tag number, trailer tag number, vehicle identification number, the bill of lading number, or the load identification number identified in the permit. An electronic version of a trip permit may be presented, if the trip permit is readily available and legible. The permitted vehicle’s size, weight, number of axles, axle spacings, and any unique characteristics must comply with the limits for that item if addressed in the permit or any amendment to that permit. Trip permits are valid only for those routes specified in the permit. Multi-trip permit vehicles are not allowed to travel on any restricted bridges or any restricted roadways identified in the permit or its attachments. No vehicle may cross any posted bridge when the vehicle exceeds the prescribed limits of the bridge.

(2) Escorts accompanying overdimensional loads as required by permit or pursuant to subsection 14-26.012(6), (7) or (8), F.A.C., are limited to:

(a) Law enforcement escorts.

(b) Escorts qualified by another state, provided that the other state has equal or more stringent standards as those required by Florida for qualified escorts and the escort has been qualified or re-qualified within the past four years.

(c) Qualified escorts:

1. Must be at least 18 years of age and must possess a valid driver’s license in the state or jurisdiction in which he or she is a resident.

2. Must have successfully completed a minimum eight hour defensive driving course as provided by a National Safety Council qualified instructor or hold a currently valid Commercial Driver’s License (Class A, B, or C). The instructor shall not be an employee of the employing escort service.

3. Must have successfully completed a minimum eight hour pilot/escort flagging course provided by a Department vendor.

4. Shall maintain in his or her possession, for prompt presentation upon request by a law enforcement person or Department representative, a copy or copies of the qualification document or documents verifying completion of the required qualification courses.

5. Shall be requalified every four years by successfully completing a four hour refresher course provided by a Department vendor.

(3) Escort Vehicle and Equipment Requirements for Qualified Escorts.

(a) Escort Vehicles.

1. Escort vehicle(s) must be a single unit vehicle with a gross vehicle weight rating of at least 2,000 pounds and less than 26,000 pounds. The vehicle must be properly licensed, registered, and operated by a qualified escort.

2. Identification signs or placards showing the name of the company or the owner or driver of the escort vehicle must be in a conspicuous place on both the right and left sides of the escort vehicle. The signs or placards shall be at least 8 inches × 12 inches, or contain the equivalent square inches, and shall also contain the telephone number of the owner or driver plainly legible and visible to the motoring public.

3. All escort vehicles must be equipped with high visibility rotating, strobe or flashing class 2 amber warning lights mounted so as to be seen by all approaching traffic at a distance of at least 500 feet.

4. Escort vehicles shall display either a bumper mounted or a roof mounted yellow sign (or may display both) reading “OVERSIZE LOAD” with black letters with a minimum brush stroke of 10 inches high and 1 1/2 inches wide, which must be visible from front and rear.

5. Two flags, either red or fluorescent orange in color, which must be at least 18 inches × 18 inches, shall be mounted at approximately a 40 to 70 degree angle on the escort vehicle’s roof rack.

(b) On Board Equipment. During escort operations, all escort vehicles shall have on board the following equipment and such equipment shall be in working order:

1. Operable two-way electronic communications. Qualified escorts must have a method for maintaining verbal communication with the driver of the permitted load at all times during movements.

2. One Class ABC fire extinguisher, minimum five pounds.

3. “STOP” and “GO” or “STOP” and “SLOW” paddles a minimum 18 inches in diameter with 6 inch high letters.

4. A high visibility, fluorescent class 2 safety vest for flagging during daytime hours or a high visibility, fluorescent class 3 safety vest when flagging at night.

5. One hand-held flag, either red or fluorescent orange in color, which must be at least 12 inches × 12 inches.

6. Two warning signs (yellow with black lettering) with a minimum brush stroke of 12 inches high and 1 1/2 inches wide. Each warning sign shall have a total dimension of not less than 7 feet long by 18 inches high. These signs shall be used in the event the permitted vehicle or load loses its sign(s).

7. Three 36 inch traffic cones. Traffic cones must be reflective if used at night.

8. For over height loads, the lead vehicle must have a height indicator, i.e., height pole, used to determine vertical clearance. This device must be manufactured of non-conductive and non-destructive material and must be positioned at a height of at least 6 inches above the height of the load being escorted.

(4) Escort Functions. Escorts are required to watch and direct traffic or the load to ensure public safety. Escorts may, when actively escorting permitted loads, perform necessary traffic control functions as defined in section 316.079(2), F.S. No escort or escort vehicle may be used to perform any other function that could distract from the escort responsibilities. The total number of escorts required will be determined based upon safety considerations. If one escort is required for an over width load, the escort shall precede the load on two lane highways or follow the load on four lane divided highways. If two escorts are required, one must precede the load and one must follow. If the load is over length only, the escort vehicle shall be in the rear of the load at all times. Escorts shall operate no more than 300 feet in front of or behind the load unless road conditions or permit stipulations dictate otherwise. Escorts equipped with a vertical height indicator must precede the load at a distance which allows the permitted vehicle to take evasive action when approaching overhead obstructions. Escort vehicles in the process of escorting a permitted vehicle or load must proceed through weigh stations and must not bypass such stations. The Permittee is responsible for providing the escort with a copy of the permit prior to the move.

(5) Safety Requirements and Restrictions for Permitted Load and Vehicle.

(a) Flags. Flags shall be clean, have high visibility, and be at least 18 inches × 18 inches. They shall be displayed so as to wave freely on all four corners of the vehicle and at the extreme ends of all protrusions, projections, or overhangs.

(b) Warning Lights.

Required Display. Vehicles or loads exceeding 10 feet in width, 80 feet in length (or over 3 feet of front overhang for self-propelled equipment), or 14 feet 6 inches in height shall have warning lights which shall:

1. Be class 2 high visibility rotating, strobe or flashing amber warning lights; and,

2. Be mounted so as to be seen by all approaching traffic at a distance of at least 500 feet.

(c) Warning Signs.

1. Required Display. Vehicles or loads exceeding 10 feet in width, 80 feet in length, or 14 feet 6 inches in height.

2. Each warning sign shall:

a. Consist of black letters 12 inches high with a brush stroke of not less than 1 1/2 inches wide on a yellow background.

b. State “OVERSIZE LOAD.”

c. Have a total dimension of not less than 7 feet long by 18 inches high.

d. Be either bumper mounted or roof mounted. If one of the signs is roof mounted then, the other sign must be at the rear of the towed unit or at the rear of the load. Voids (holes) may be cut in warning signs as signs must not cover any vehicle light or reflector.

(d) Movement During Periods of Poor Visibility. No travel is allowed when horizontal visibility is less than 1,000 feet. Vehicles which are underway when inclement weather occurs must exit the road at the first available location and park until the weather clears or until road conditions improve.

(e) Movements on Weekends and Holidays. Unless otherwise noted on the permit, movements are prohibited on weekends and holidays. A government entity, meeting the criteria of Rule 14-26.00425, F.A.C., shall be allowed to travel all days, all hours with a valid permit.

(f) Nighttime movement. When the criteria of Rules 14-26.00425 and 14-26.012, F.A.C., are met, trip or multi-trip permits shall be issued providing:

1. Nighttime travel is recommended by the Department’s District Traffic Engineering Office(s) or determined to be a requirement of the permit by the Office of Maintenance.

2. Law enforcement escort(s) are used.

3. Warning lights shall delineate the shape and size of the load.

4. The sides and rear of trailers and loads shall be lighted in the manner prescribed in 49 C.F.R. sections 393.11 through 393.26, F.S., as required by section 316.302(1)(a), F.S.

(6) All vehicles, including vehicles equipped with an automatic vehicle identification system, must stop at open weigh stations. Vehicles operating under an internal (inner) bridge permit may bypass an open weigh station when a Department approved electronic credentialing device instructs the vehicle to proceed.

(7) Width Limitations.

(a) Vehicles up to 10 feet. When the criteria of Rule 14-26.00425, F.A.C., are met, trip or multi-trip permits shall be issued. Movement is permitted all days, during daytime hours only. Flags are required.

(b) Vehicles over 10 feet up to 12 feet. When the criteria of Rule 14-26.00425, F.A.C., are met, trip or multi-trip permits shall be issued. Movement permitted daytime hours only, excluding holidays. Flags, warning signs, and warning lights are required. Except for local moves, this is the maximum width allowed on a straight truck.

(c) Vehicles over 12 feet up to 14 feet. When the criteria of Rule 14-26.00425, F.A.C., are met, trip or multi-trip permits shall be issued. Movement is permitted during daytime hours only, excluding holidays. Flags, warning signs, and warning lights are required. A minimum of one escort vehicle, with escort, is required at all times.

1. All manufactured buildings, manufactured homes, mobile homes, modular buildings, sheds, and swimming pools shall use a minimum of four warning lights mounted, with two on the front and two on the rear at each corner of the towed or hauled unit.

2. All other loads shall have a minimum of two warning lights mounted with one on the front and one on the rear of the load.

3. On roadway lanes less than 12 feet wide, bridges with less than 30 feet curb to curb, and in rural areas with traffic volume greater than 12,000 Average Daily Traffic (ADT) per lane or in urbanized areas (more than 50,000 population) with ADT greater than 8,000 vehicles per lane, two qualified escorts are required except on loads with a minimum of four warning lights mounted two in front and two in the rear of the towed or hauled unit.

4. No movement will be allowed in congested areas during peak traffic hours unless specifically authorized by permit.

(d) Vehicles over 14 feet up to 16 feet. When the criteria of Rule 14-26.00425, F.A.C., are met, trip permits only shall be issued. Movement is permitted daytime hours only, excluding holidays. Flags, warning signs, and warning lights are required. Two qualified escorts are required at all times during the move, one in the front and one in the rear of the load.

1. All loads consisting of manufactured buildings, manufactured homes, mobile homes, modular buildings, sheds, and swimming pools shall use a minimum of four warning lights mounted with two on the front and two on the rear at each corner of the towed or hauled unit.

2. All other loads shall have a minimum of two warning lights mounted with one on the front and one on the rear of the load.

3. Two lane roadways shall not be used as a connector route whenever viable four lane routes are available. Requests for two lane roadways as connector routes may require justification from the customer and ultimate approval from the Department. No movement will be allowed in congested areas during peak traffic hours.

4. The maximum width for manufactured buildings is 16 feet.

(e) Vehicles over 16 feet. When the criteria of Rule 14-26.00425, F.A.C., are met, only trip permits shall be issued. Same as criteria for “Vehicles over 14 feet up to 16 feet” except movement will be restricted to local moves. Applications for permits over 16 feet wide are subject to review by the Department’s District Traffic Engineering Office(s).

1. Two qualified escorts are required when travelling on a limited access facility during daytime hours only.

2. One law enforcement escort and one qualified escort are required when travelling on a limited access facility during nighttime hours.

3. Two law enforcement escorts are required at all times when travelling on state maintained roadways (excluding limited access facilities).

4. Items must be moved by rail, air, or water when possible.

5. Trip permit requests for vehicles over 22 feet wide will require an affidavit verifying that the proposed route has adequate horizontal clearance to accommodate the requested width in addition to two feet on each side.

(8) Height Limitations.

(a) Vehicles up to 14 feet 6 inches. When the criteria of Rule 14-26.00425, F.A.C., are met, trip or multi-trip permits shall be issued. Movement is permitted all days and all hours. Except for local moves, this is the maximum height for loads hauled on straight trucks.

(b) Vehicles over 14 feet 6 inches up to 16 feet. When the criteria of Rule 14-26.00425, F.A.C., are met, trip or multi-trip permits shall be issued. Movement is permitted daytime hours only, excluding holidays. Flags, warning signs, and warning lights are required. A minimum of two warning lights are required; one mounted on the front and one on the rear of the load. An escort vehicle with a vertical height indicator is required to precede the load at a distance which allows the permitted vehicle to take evasive actions when approaching overhead obstructions.

(c) Vehicles over 16 feet. When the criteria of Rule 14-26.00425, F.A.C., are met, trip or multi-trip permits shall be issued. Multi-trip permits shall be limited to vehicles up to 18 feet. Trip permit requests for movement of vehicles over 18 feet high will require an affidavit verifying the proposed route has clearance to accommodate the request height plus six inches. Movement is permitted during daytime hours only, excluding holidays. Flags, warning signs, and warning lights are required. A minimum of two warning lights are required with one mounted on the front and one on the rear of the load. In addition, movement is restricted to local moves only.

1. One law enforcement escort in addition to one qualified escort is required. The qualified escort must precede the load with a vertical height indicator at a distance which allows the permitted vehicle to take evasive actions when approaching overhead obstructions.

2. Appropriate utility personnel will also be required whenever the load will encounter low barriers such as overhead structures, traffic signals, and low wires.

(9) Length Limitations.

(a) Vehicles up to 80 feet. When the criteria of Rule 14-26.00425, F.A.C., are met, trip or multi-trip permits shall be issued. Movement is permitted all days and all hours.

1. Rear overhang is limited to a maximum of 10 feet during nighttime movement unless otherwise stated on the permit.

2. When overhang exceeds 4 feet, a warning light is required on the top of the vehicle. At the extreme rear of the load there must be two red lamps and two red reflectors on each side of the load. Each required warning lamp shall be visible from a distance of at least 500 feet.

(b) Vehicles over 80 feet. When the criteria of Rule 14-26.00425, F.A.C., are met, trip or multi-trip permits shall be issued. Movement is permitted during daytime hours only, excluding holidays. Flags, warning signs, and warning lights are required. A minimum of two warning lights are required to be mounted: one on the front and one on the rear of load.

1. No movement will be allowed in congested areas during peak traffic hours for vehicles over 85 feet in length unless specifically authorized by permit.

2. Truck tractor semi-trailers with three points of articulation are allowed up to 105 feet in length without an escort.

3. One qualified escort is required when the length exceeds 95 feet.

4. Two qualified escorts are required when the length exceeds 150 feet unless the vehicle is traveling on a limited access facility, then only one qualified escort is required.

5. One law enforcement escort and one qualified escort are required when the length exceeds 250 feet.

6. Maximum length for a manufactured homes, modular units and portable buildings is 120 feet provided the length of the towed housing does not exceed 81 feet, including all overhangs and tongue.

7. Maximum length of multiple sections or single units of manufactured buildings on a trailer is 80 feet.

(c) Self-Propelled Equipment Length Limitations. When the criteria of Rule 14-26.00425, F.A.C., are met, trip or multi-trip permits shall be issued. For all self-propelled equipment, the boom must be fully retracted. Nightime movement requires that the front overhang has a minimum of 80 inches clearance above the roadway. In addition, no movement is allowed on limited access facilities with units designed for off road use. In addition the following restrictions will apply:

1. Total length up to 80 feet.

a. Front Overhang over 3 feet up to 9 feet. Movement is permitted on all days, all hours. A warning light is required to be mounted at the extreme end of the protrusion in such a way as to be seen by all approaching traffic.

b. Front Overhang over 9 feet. Movement is permitted all days, during daytime hours only. A warning light is required to be mounted at the extreme end of the protrusion in such a way as to be seen by all approaching traffic.

2. Total Length over 80 feet. Movement is permitted daytime hours only, excluding holidays. Flags and warning signs are required. A warning light is required to be mounted at the extreme end of the protrusion in such a way as to be seen by all approaching traffic.

(10) Multiple Loading. When the criteria of Rule 14-26.00425, F.A.C., are met, trip or multi-trip permits shall be issued providing:

(a) Multiple loading does not cause the dimensions of the load to exceed those limits established in section 316.515, F.S.; and,

(b) Multiple loading does not cause the gross vehicle weight to exceed those limits established in section 316.535, F.S.

(c) Vehicles will only be allowed to exceed the gross vehicle weight limits established in section 316.535, F.S., when:

1. Attachments (e.g. blade, rake, bucket, counterweights) that are a normal part of the equipment have been removed to reduce the size of the load for safety reasons. A maximum of two attachments may be transported if they are attachable to the equipment and necessary for operation.

2. The gross vehicle weight does not exceed 100,000 pounds and no more than two overlength items are being hauled.

3. Operating under a divisible load permit.

(11) Designated Permits.

(a) “Implements of Husbandry,” farm equipment, agricultural trailers, and forestry equipment are exempt pursuant to section 316.515, F.S., from certain size requirements. However, these vehicles are not exempt from any overweight limitations set forth in section 316.535, F.S. When the vehicle configurations exceed any of the weight limits described in section 316.535, F.S., an overweight permit must be obtained from the Department.

(b) Movement of an empty truck tractor semi-trailer up to 11 feet in width and not over 105 feet in length, traveling on or within five miles of limited access roadways, when operating with an existing valid permit will be allowed to travel during nighttime hours. Warning lights, flags, signs, and escorts will be required as permit conditions based upon the dimensions of the load when traveling empty during nighttime hours. Extra axles and stingers may be hauled on the trailer to reduce overall dimensions for safety purposes.

(c) Semi-trailers with a kingpin greater than 41 feet and a trailer length up to 57 feet 6 inches may haul a divisible load when operating in a truck tractor semi-trailer combination with a valid trip or multi-trip permit.

(d) Truck tractor semi-trailer combinations hauling automobiles or boats may obtain a trip or multi-trip permit, regardless of trailer length, when the overall length does not exceed 80 feet excluding overhang. This applies to both stinger and non-stinger steered vehicles.

(e) Straight truck and trailer combinations hauling automobiles/boat may obtain a trip or multi-trip permit when the overall length does not exceed 80 feet including overhang.

(f) Trip or multi-trip permits will be issued to truck tractor semi-trailer combinations to deviate from inner-bridge requirements when traveling on interstate highways and when the criteria of Rule 14-26.00425, F.A.C., are met. These vehicles are not allowed to exceed the external bridge or axle weight limitations described in section 316.535, F.S.

(g) A vehicle operating under a valid permit with a law enforcement escort, may enter Florida at the Alabama Line on I-10 and proceed to the eastbound Pensacola Weigh Station or exit Florida at the Alabama Line on I-10 when leaving the westbound Pensacola Weigh Station during nighttime hours.

(12) Wrecker Permits.

(a) When the combined weight of the wrecker and disabled vehicle being towed exceeds the maximum weight limits established by Section 316.535, F.S., trip or multi-trip permits shall be issued if all the criteria of Rule 14-26.00425, F.A.C., are met.

(b) Escort requirements for towing disabled permitted vehicles shall be as prescribed in the original permit or amendment thereto for the towed vehicle.

(c) It is the responsibility of the wrecker operator to secure permits necessary to cover the attached load.

(d) In all instances where legal weight is exceeded, all available brakes on the towed vehicle will be functional and in operation at all times while being towed.

(e) An illegally loaded vehicle shall not become legal by being attached to a permitted wrecker.

(f) The combined gross vehicle weight of the wrecker and towed vehicle shall not exceed 140,000 pounds.

(g) The combined length of the wrecker and the towed vehicle shall not exceed 135 feet.

(h) The permitted vehicle combination must be operated with attached map(s) showing acceptable routes for specific axle and vehicle configurations.

Rulemaking Authority 316.515, 316.550, 334.044(2) FS. Law Implemented 316.228, 316.515, 316.550, 334.044(28) FS. History–New 8-26-82, Amended 12-6-83, Formerly 14-26.12, Amended 9-15-87, 5-2-90, 7-21-91, 6-23-96, 11-10-98, 2-1-10, 10-4-10, 2-5-13, 8-23-16, 3-9-17, 4-24-18.

## 14-26.013 Permits to Move Buildings.

Rulemaking Authority 316.550, 334.044(2) FS. Law Implemented 316.550 FS. History–New 8-26-82, Formerly 14-26.13, Amended 7-21-91, 6-23-96, Repealed 2-1-10.

## 14-26.013 Permits to Move Buildings.

Rulemaking Authority 316.550, 334.044(2) FS. Law Implemented 316.550 FS. History–New 8-26-82, Formerly 14-26.13, Amended 7-21-91, 6-23-96, Repealed 2-1-10.

## 14-26.0131 Permits to Move Ocean-Going Sealed Containerized Cargo Units.

Rulemaking Authority 20.05(5), 316.550, 334.044(2) FS. Law Implemented 120.53(1)(b), 316.535, 334.044(2), (26) FS. History–New 8-26-89, Repealed 10-6-92.

## 14-26.01311 Permits to Move Sealed Containerized Loads.

(1) Definitions. For the purposes of this rule:

(a) A “Sealed Containerized Load” means a freight container with or without wheels, as defined in Title 49 C.F.R., Part 59, Sec 5901(4), Rev. 2008, incorporated herein by reference, available at https://www.flrules.org/Gateway/reference.asp?No=Ref-02204.

(b) “Destination point” means the location where the packer’s seal, law enforcement seal, or U.S. Customs’ seal is broken.

(c) “Point of origin” means the location where the packer’s seal is affixed.

(2) General. Sealed containerized loads being moved via a truck or trucks and rail in conjunction with a maritime shipment will be considered a “nondivisible” load, eligible for an overweight or overdimensional permit, when the following conditions are met:

(a) The sealed containerized load is being moved by a vehicle qualified to do so under the provisions of this rule:

1. From a maritime port to the destination point, or

2. From a maritime port to a railroad facility for movement to the destination point, or

3. From the point of origin to a maritime port, or

4. From the point of origin to a railroad facility for movement to a maritime port; and,

(b) The sealed containerized load retains the original unbroken seal from its point of origin, a seal placed by law enforcement, or a replacement U.S. Customs’ seal throughout its transit until reaching its destination point.

(3) Required On-Board Documents.

(a) The operators of vehicles transporting sealed containerized loads by permits issued pursuant to this rule shall at all times have on board and make available for inspection a hard copy of at least one of the following documents:

1. A short form master bill of lading,

2. A copy of an electronically transmitted way bill, or

3. A completed U.S. Customs Service Authority to move (Form 75-12) valid for the permitted load.

(b) The document(s) in paragraph (a) shall include the following readily identifiable information:

1. Consignor,

2. Point of origin,

3. Consignee,

4. Point of destination; and,

5. Either the number of the packer’s cargo seal or the number of the U.S. Customs seal.

(4) No Straight Trucks. Because of the nature of the load to be carried and the potential for increased wear to the highway from vehicles so loaded, no straight truck, as defined in Section 316.003(70), F.S., shall be eligible for a permit to haul sealed containerized loads.

(5) Trip or Multi-Trip Permits. When applying for a trip or multi-trip permit to transport sealed containerized loads, the hauler must submit an application in accordance with subsection 14-26.00411(4), F.A.C., and include:

(a) Maximum gross weight of the vehicle and load;

(b) Axle spacing (center to center of each axle);

(c) The total number of axles and total weight on each axle of the vehicle/vehicle combination;

(d) The origin and destination of the highway move (for trip permits);

(e) Either the number of the packer’s cargo seal or the number of the U.S. Customs’ seal;

(f) The State highway(s) requested to be traveled (for trip permits).

(6) Overall Gross Vehicle Weight. Vehicles operating under a permit issued pursuant to this rule shall not exceed an overall gross vehicle weight of 100,000 pounds.

(7) Axle Spacings. All vehicles operating under a permit issued pursuant to this rule shall meet the minimum axle spacing requirements described in the permit.

(8) Number of Axles. All vehicles operating under a permit issued pursuant to this rule shall have a minimum of five load-bearing axles in operation at all times during movement.

(9) Outer Bridge Length. All vehicles operating under a permit issued pursuant to this rule shall have an outer bridge length of 51 feet or greater.

Rulemaking Authority 316.550, 334.044(2) FS. Law Implemented 316.535, 316.550, 334.044(27) FS. History–New 9-14-93, Amended 6-23-96, 2-1-10, 10-4-10, 2-5-13, 3-9-17.

## 14-26.014 Non-Compliance.

(1) Suspension or revocation of permits.

(a) The Department will suspend or revoke a multi-trip or trip permit for a specified period of time for the following:

1. The permittee fails to comply with the regulations of this rule chapter or the requirements of Florida Statutes.

2. The permittee has submitted a false, deceptive, or fraudulent permit application.

3. The permittee fails to comply with the terms of the permit.

4. The permittee travels on other than approved routes.

5. The permittee fails to submit a list of specified routes over which the load can or cannot travel, when required.

6. The permittee fails to pay fees/penalties owed to the Department of Transporation, the Department of Highway Safety and Motor Vehicles or their agent(s).

7. The company has been placed out-of-service based upon a compliance review performed by Florida Highway Patrol or Federal Motor Carrier Safety Administration.

8. The Department determines that continued operation under an existing valid permit poses a safety issue for state owned bridges or roadways.

(2) Denial of future permits.

In addition to suspension or revocation of a multi-trip or trip permit as set forth in subsection (1) of this rule, the Department will deny issuance of future permits as follows:

(a) First 	Written warning

(b) Second	30 Days

(c) Third	90 Days

(d) Fourth	12 Months

Rulemaking Authority 316.550, 334.044(2) FS. Law Implemented 316.550 FS. History–New 8-26-82, Amended 12-6-82, 3-18-84, Formerly 14-26.14, Amended 9-15-87, 4-22-92, 6-23-96, 1-17-99, 2-1-10, 8-23-16, 3-9-17.

## 14-26.015 Penalties.

(1) Any vehicle in violation of any permit criteria, or operating without a permit where one is required, will be required to correct all offending irregularities or obtain a new permit based on the vehicle’s actual load prior to release of the vehicle. Additionally, the following penalties for violation of permit requirements will apply:

(a) An oversize or overweight vehicle being operated without a permit will have penalties assessed in accordance with Sections 316.545 and 316.516, F.S.

(b) A vehicle operated with a valid permit which exceeds the weight criteria contained in the permit, will be assessed a penalty for every pound or portion thereof exceeding the permitted weight as provided in section 316.545, F.S.

(c) A vehicle operated with a valid permit which exceeds the dimensional criteria contained in the permit, will be assessed a penalty for every foot or portion thereof exceeding the permitted dimension, as provided in section 316.516, F.S., except that the total penalty for the vehicle shall not exceed $1,000.00, as provided in section 316.550(10)(b), F.S.

(d) A vehicle operated with a valid permit which vehicle violates an operational or safety provision contained in the permit, will be assessed a penalty of $100.00 per safety violation (lights, flags, signs, etc.) and $250.00 per absent escort, except that the total penalty for the vehicle shall not exceed $1,000.00.

(e) A vehicle operated with a valid permit which violates daytime, nighttime, or restricted hours of travel restrictions shown on the permit, which violates weekend and holiday travel restrictions shown on the permit, or which violates the restrictions against movement during periods of poor visibility, will be assessed a penalty of $1,000.00 and the vehicle will be parked at owner’s expense and responsibility until the next authorized travel period.

(f) Any vehicle operating on an oversize/overweight permit (excluding inner bridge permits) which bypasses an open weigh station will be assessed a penalty of $1,000.00.

(g) Any vehicle operating on a forged or altered permit will be assessed a penalty of $1,000.00 in addition to penalties assessed for size/weight violations.

(2) Null and Void Criteria. Any vehicle found to be operating under one or more of the following conditions shall be determined to be out of conformity with the provisions of the permit, in which case the vehicle is considered to be in non-compliance and the permit will be declared to be null and void for that vehicle for that trip. Penalties will be assessed as provided in sections 316.516 and 316.545, F.S., and the vehicle must remain until the load is brought into compliance or a valid permit is obtained.

(a) The vehicle does not have the required number of axles. Penalty to be assessed for the weight only.

(b) The vehicle has an expired permit. Penalty to be assessed for both weight and size.

(c) The vehicle is not on the route designated on the permit or on an approved route on the multi-trip permit attachments. Penalty to be assessed for both weight and size.

(d) The vehicle is a self-propelled truck crane towing a motor vehicle that exceeds the 5,000 pound limit allowed in Section 316.550, F.S. Penalty to be assessed for weight only.

(e) The vehicle is operating with a permit which has been altered or forged. Penalty to be assessed for both weight and size.

(f) The vehicle is not as represented by the facts on the permit. Penalty to be assessed for both weight and size. This violation will not be applicable if it duplicates another violation noted in a specific citation.

(g) The vehicle contains multiple loading (except as allowed per this rule). Penalty to be assessed based upon the nature of the violation (weight or size).

(h) The vehicle has an outer-bridge dimension which is less than the minimum specified on the permit. Penalty to be assessed for weight only.

(i) The vehicle is being operated under a multi-trip permit and the permit is not accompanied by the required attachments described in the permit. Penalty to be assessed based upon the nature of the violation (weight or size).

(j) The hauler does not produce a survey letter as described in subsection 14-26.00411(5), F.A.C., when requested by law enforcement or a weight inspector. Penalty to be assessed for size only.

(k) The vehicle does not have a valid restricted tag or is not registered for 80,000 pounds gross vehicle weight when transporting an oversized/overweight load. Penalty to be assessed for weight only.

Rulemaking Authority 316.550, 334.044(2) FS. Law Implemented 316.516(4), 316.550(8), (10) FS. History–New 6-23-96, Amended 11-10-98, 2-1-10, 10-4-10, 2-5-13, 8-23-16, 3-9-17, 4-24-18.