# CHAPTER 62-297

# STATIONARY SOURCES ‒ EMISSIONS MONITORING

# 62-297.100	Purpose and Scope (Repealed)

# 62-297.310	General Emissions Test Requirements

# 62-297.320	Standards for Persons Engaged in Visible Emissions Observations

# 62-297.401	Compliance Test Methods (Repealed)

# 62-297.440	Supplementary Test Procedures

# 62-297.450	EPA VOC Capture Efficiency Test Procedures

# 62-297.520	EPA Continuous Monitor Performance Specifications (Repealed)

# 62-297.620	Exceptions and Approval of Alternate Procedures and Requirements

## 62-297.100 Purpose and Scope.

Rulemaking Authority 403.061 FS. Law Implemented 403.021, 403.031, 403.061, 403.087 FS. History–Formerly 17-2.700(1)(a), 17-297.100, Amended 11-23-94, 3-13-96, Repealed 2-16-12.

## 62-297.310 General Emissions Test Requirements.

(1) Applicability. Unless otherwise stated in a specific rule, permit, or other order, the general requirements set forth in subsections 62-297.310(2) through (10), F.A.C., shall be used for regulated stationary sources’ emissions tests for comparison with air pollution emission-limiting standards that are enforceable under state law. An emissions test is an emissions rate test, a concentration test, or an opacity test.

(2) Required Number of Test Runs. For emission rate or concentration limitations, an emissions test shall consist of three valid test runs to determine the total air pollutant emission rate or concentration through the test section of the stack or duct. A valid test run is a test run that meets all requirements of the applicable test method. An emissions test shall also consist of three distinct determinations of any applicable process parameters corresponding to the three distinct test run time periods during which the emission rate or concentration was measured when such data are needed in conjunction with emissions data to compare the emissions test results with the applicable emission limiting standards. Such data shall be obtained pursuant to subsection 62-297.310(6), F.A.C. The three required test runs shall be completed within one consecutive five-day period. In the event that a sample is lost or one of the three runs must be discontinued because of circumstances beyond the control of the owner or operator, and a valid third run cannot be obtained within the five day period allowed for the test, results of the two valid runs shall be accepted, provided that the arithmetic mean of the results of the two valid runs is at least 20% below the allowable emission limiting standard.

(3) Operating Conditions during Emissions Testing. Testing of emissions shall be conducted with the emissions unit operating at the testing capacity as defined below. If it is impracticable to test at the testing capacity, an emissions unit may be tested at less than the testing capacity. If an emissions unit is tested at less than the testing capacity, another emissions test shall be conducted and completed no later than 60 days after the emissions unit operation exceeds 110% of the capacity at which its most recent emissions test was conducted.

(a) Combustion Turbines. (Reserved)

(b) All Other Sources. Testing capacity is defined as at least 90 percent of the maximum operation rate specified by the permit.

(4) Calculation of Emission Rate or Concentration. The emission rate or concentration used for comparison with the relevant standard shall be the arithmetic average of the emission rate or concentration determined by each of the three valid test runs unless otherwise specified in an applicable rule or test method. Data collected during periods of soot blowing shall not be excluded from any calculation of emission rate or concentration.

(5) Required Sampling Times and Observation Periods. Unless otherwise specified in an applicable test method, rule, permit, or other order, the owner or operator shall conduct emissions tests in accordance with the following procedures:

(a) Emission Rate or Concentration Tests. The required sampling time for each test run shall be no less than one hour and no greater than four hours, and the sampling time at each sampling point shall be of equal intervals of at least two minutes, except that for operations that are typically completed within less than the minimum required sampling time, the duration of each test run shall include each occurrence of the operation during the minimum required sampling time. The test period shall include the period of typical operation during which the highest representative emissions are expected to occur.

(b) Opacity Tests. When EPA Method 9 is specified as the applicable opacity test method, the required minimum period of observation for a visible emissions test shall be 60 minutes for emissions units that are subject to a multiple-valued opacity standard and 30 minutes for all other emissions units, except that for batch, cyclical processes, or other operations that are typically completed within less than the minimum observation period, the period of observation shall include each occurrence of the operation during the minimum observation period. The opacity test observation period shall include the period during which the highest opacity emissions can reasonably be expected to occur.

(6) Determination of Process Parameters.

(a) Required Process Equipment. The owner or operator of an emissions unit for which emissions tests are required shall install, operate, and maintain equipment or instruments necessary to determine process parameters, when such data are needed in conjunction with emissions data to compare emissions test results with applicable emission limiting standards.

(b) Accuracy of Process Measurement Equipment. Equipment or instruments used to directly or indirectly determine process parameters shall be calibrated and adjusted so as to determine the value of the process parameter to within 10 percent of its true value.

(7) Required Emissions Testing Facilities.

(a) The owner or operator of an emissions unit, for which an emissions test other than a visible emissions test is required, shall provide emissions testing facilities that meet the requirements of 40 CFR 60.8(e), adopted and incorporated in Rule 62-204.800, F.A.C.

(b) Permanent Emissions Testing Facilities. The owner or operator of an emissions unit, for which an emissions test other than a visible emissions test is required on at least an annual basis, shall install and maintain permanent emissions testing facilities.

(c) Temporary Emissions Testing Facilities. The owner or operator of an emissions unit that is not required to conduct an emissions test on at least an annual basis may use permanent or temporary emissions testing facilities. If the owner or operator chooses to use temporary emissions testing facilities on an emissions unit, and the Department elects to test the unit, such temporary facilities shall be installed on the emissions unit within 5 days of a request by the Department and remain on the emissions unit until the test is completed.

(8) Frequency of Emissions Tests. The following provisions apply only to those emissions units that are subject to an emissions-limiting standard for which emissions testing is required.

(a) Annual Emissions Tests Required.

1. Where used in Rules 62-210.310, 62-297.310, or Chapter 62-296, F.A.C., to refer to frequency of required emissions tests, the terms “annual,” “annually,” and “annually thereafter” shall mean no less frequently than once every calendar year (January 1 – December 31).

2. Unless exempted by subparagraph 62-297.310(8)(a)5., F.A.C., the owner or operator shall have an emissions unit tested annually for each of the following pollutants that has an emissions-limiting standard for which emissions testing is required:

a. Each hazardous air pollutant regulated by 40 C.F.R. Part 61, adopted and incorporated by reference at Rule 62-204.800, F.A.C.; and,

b. Any other regulated air pollutant, as defined at Rule 62-210.200, F.A.C., or a pollutant designated as a surrogate to a regulated air pollutant by an applicable rule or order, if allowable emissions equal or exceed 100 tons per year.

3. Unless exempted by subparagraph 62-297.310(8)(a)5., F.A.C., the owner or operator shall have an emissions unit tested annually for visible emissions, if there is an applicable standard other than the general opacity standard of subparagraph 62-296.320(4)(b)1., F.A.C.

4. Unless exempted by subparagraph 62-297.310(8)(a)5., F.A.C., the owner or operator shall have an emissions unit tested annually if a rule, permit or other order issued after March 9, 2015, requires an initial emissions test but is silent as to the frequency of additional testing. A rule, permit, or other order that states that no further testing is required after an initial test, or which expressly lists or describes the tests that shall be conducted annually, is not considered silent as to the frequency of additional testing. Annual testing is not required where a permit or other order issued prior to March 9, 2015, is silent as to the frequency of additional testing.

5. Exemptions from subparagraphs 62-297.310(8)(a)2., 3., and 4., F.A.C.

a. An annual emissions test shall not be required for any pollutant for which a rule, permit, or other order requires emissions testing at some other specific frequency. If multiple applicable rules, permits, or other orders, other than subparagraphs 62-297.310(8)(a)2., 3., and 4., F.A.C., require different testing frequencies, testing must comply with the frequency requirements of each such rule, permit, or order.

b. An annual emissions test shall not be required for any pollutant for which a rule, permit, or other order requires that the pollutant emissions be measured by a continuous emission monitoring system and, either that system meets the performance specifications and quality assurance and quality control measures of 40 CFR part 60, adopted and incorporated in Rule 62-204.800, F.A.C., or that system meets the performance specifications and quality assurance and quality control measures of 40 C.F.R. part 75, adopted and incorporated in Rule 62-204.800, F.A.C.

c. An annual emissions test shall not be required for visible emissions for which a rule, permit, or other order requires that emissions be measured by a continuous opacity monitoring system, and that system meets the performance specifications and quality assurance and quality control measures of 40 C.F.R. part 60, adopted and incorporated in Rule 62-204.800, F.A.C., and the manufacturer’s recommended quality assurance and quality control measures.

d. An annual emissions test shall not be required for any emissions unit that operated for 400 hours or less (including during startup and shutdown) during the calendar year. If an emission unit operates for more than 400 hours during the calendar year, an emissions test shall be completed no later than 60 days after the emissions unit’s annual operation exceeds 400 hours, or by the end of the calendar year, whichever is later.

e. An annual emissions test shall not be required for any emissions unit with emissions generated solely from the combustion of fuel, provided that the emissions unit does not burn any liquid fuel or solid fuel or fuel blend for more than 400 hours combined, other than during startup, during the calendar year. If an emissions unit’s liquid fuel or solid fuel or fuel blend burning exceeds 400 hours combined during the calendar year, other than during startup, an emissions test shall be completed no later than 60 days after the emissions unit’s liquid fuel or solid fuel or fuel blend burning exceeds 400 hours combined, or by the end of the calendar year, whichever is later.

f. An annual emissions test shall not be required for each fuel-specific emissions limit, provided the fuel or fuel blend subject to a fuel-specific limit was not burned for more than 400 hours, other than during startup, during the calendar year. If an emissions unit burns a fuel or fuel blend subject to a fuel-specific emission limit for more than 400 hours, other than during startup, during the calendar year, an emissions test for that fuel or fuel blend shall be completed no later than 60 days after the unit’s burning of that fuel or fuel blend exceeds 400 hours, or by the end of the calendar year, whichever is later.

g. An emissions unit shall not be required to start up for the sole purpose of conducting an emissions test to meet the frequency requirements of subsection 62-297.310(8), F.A.C. In such a case, an emissions test shall be completed no later than 60 days after the emissions unit next starts up.

h. An emissions unit permitted to burn multiple fuels or fuel blends shall not be required to switch fuels for the sole purpose of conducting an annual emissions test to meet the frequency requirements of subsection 62-297.310(8), F.A.C.  In such a case, an emissions test shall be completed no later than 60 days after a switch is made to burn the fuel or fuel blend for which testing is required.

i. An annual emissions test for visible emissions shall not be required for emissions units exempted from air permitting pursuant to paragraph 62-210.300(3)(a) or (b), F.A.C.; emissions units determined to be insignificant pursuant to paragraph 62-213.430(6)(b), F.A.C.; or emissions units authorized pursuant to the general permit provisions in subsection 62-210.300(4), F.A.C., unless the general permit specifically requires such testing.

(b) Emissions Tests Prior to Obtaining an Air Operation Permit.

1. Unless exempted by subparagraph 62-297.310(8)(b)3., F.A.C., prior to obtaining an initial or renewal air operation permit for any emissions unit that is subject to any emission-limiting standard, the owner or operator shall have an emissions test conducted for each such standard to assist in providing reasonable assurance, per Rule 62-4.070, F.A.C., that the emission-limiting standard can be met and shall submit the test report as specified in subsection 62-297.310(10), F.A.C. For an emissions unit at a Title V source, such prior emissions testing is not required provided that an emissions testing compliance plan is included in the Title V permit.

2. For the purpose of renewal of an air operation permit, the owner or operator may satisfy the requirements of subparagraph 62-297.310(8)(b)1., F.A.C., for any emissions unit by submitting the most recent emissions test, as specified in subsection 62-297.310(10), F.A.C., provided such test occurred within the term of the current operating permit.

3. Exemptions from subparagraph 62-297.310(8)(b)1., F.A.C.

a. An emissions test shall not be required for any pollutant for which a rule, permit, or other order requires that the emissions be measured by a continuous emission monitoring system and, either that system meets the performance specifications and quality assurance and quality control measures of 40 C.F.R. part 60, adopted and incorporated in Rule 62-204.800, F.A.C., or that system meets the performance specifications and quality assurance and quality control measures of 40 C.F.R. part 75, adopted and incorporated in Rule 62-204.800, F.A.C.

b. An emissions test shall not be required for visible emissions for which a rule, permit, or other order requires that emissions be measured by a continuous opacity monitoring system, and that system meets the performance specifications and quality assurance and quality control measures of 40 C.F.R. part 60, adopted and incorporated in Rule 62-204.800, F.A.C., and the manufacturer’s recommended quality assurance and quality control measures.

c. For the purpose of renewal of an air operation permit, an emissions test shall not be required for any emissions unit that, in the previous five-year period of permitted operation, operated for 400 hours or less (including during startup and shutdown) during each calendar year included in the five-year period of permitted operation. The first time an emissions unit subsequently exceeds 400 hours of operation during a calendar year, emissions must be tested no later than 60 days after 400 hours of operation is exceeded in that calendar year, or by the end of that calendar year, whichever is later.

d. For the purpose of renewal of an air operation permit, an emissions test shall not be required for any emissions unit with emissions generated solely from the combustion of fuel provided that, in the previous five-year period of permitted operation, the emissions unit did not burn any liquid fuel or solid fuel or fuel blend for more than 400 hours combined, other than during startup, during each calendar year included in the five-year period of permitted operation. The first time an emissions unit subsequently burns any liquid fuel or solid fuel or fuel blend for more than 400 hours combined during a calendar year, emissions must be tested no later than 60 days after the emissions unit’s combined burning of any liquid fuel or solid fuel or fuel blend exceeds 400 hours in that calendar year, or by the end of that calendar year, whichever is later.

e. An emissions test shall not be required for each fuel-specific emissions limit prior to the renewal of an air operation permit for an emissions unit provided that, in the previous five-year period of permitted operation, the fuel or fuel blend subject to a fuel-specific limit was not burned for more than 400 hours, other than during startup, during each calendar year included in the five-year period of permitted operation. The first time an emissions unit subsequently burns a fuel or fuel blend subject to a fuel-specific emission limit for more than 400 hours, other than during startup, during any calendar year, an emissions test for that fuel or fuel blend must be completed no later than 60 days after the emissions unit’s burning of that fuel or fuel blend exceeds 400 hours in that calendar year, or by the end of that calendar year, whichever is later.

f. An emissions unit shall not be required to start up for the sole purpose of conducting an emissions test to meet the frequency requirements of subsection 62-297.310(8), F.A.C. In such a case, an emissions test shall be completed no later than 60 days after the emissions unit starts up.

g. An emissions unit permitted to burn multiple fuels or fuel blends shall not be required to switch fuels for the sole purpose of conducting the emissions test to meet the frequency requirements of subsection 62-297.310(8), F.A.C. In such a case, an emissions test shall be completed no later than 60 days after a switch is made to burn the fuel or fuel blend for which testing is required.

h. An emissions test for visible emissions shall not be required for emissions units exempted from air permitting pursuant to paragraph 62-210.300(3)(a) or (b), F.A.C.; emissions units determined to be insignificant pursuant to paragraph 62-213.430(6)(b), F.A.C.; or emissions units authorized pursuant to the general permit provisions in subsection 62-210.300(4), F.A.C., unless the general permit specifically requires such testing.

(c) Special Compliance Tests. When the Department, after investigation, has good reason (such as complaints, increased visible emissions or questionable maintenance of control equipment) to believe that any applicable emission standard contained in a Department rule or in a permit issued pursuant to those rules is being violated, it shall require the owner or operator of the emissions unit to conduct compliance tests which identify the nature and quantity of pollutant emissions from the emissions unit, unless the Department obtains other information sufficient to demonstrate compliance. The owner or operator of the emissions unit shall provide a report on the results of said tests to the Department in accordance with the provisions of subsection 62-297.310(10), F.A.C.

(9) Scheduling and Notification. At least 15 days prior to the date on which each required emissions test is to begin, the owner or operator shall notify the air compliance program identified by permit, unless shorter notice is agreed to by the appropriate air compliance program. The notification shall include the date, time, place of each such test, Facility ID Number, Emission Unit ID Number(s) and description(s), Emission Point Number(s) and description(s), test method(s), pollutant(s) to be tested, along with the name and telephone number of the person who will be responsible for conducting such test(s) for the owner or operator. If a scheduled emissions test needs to be re-scheduled, the owner or operator shall submit to the appropriate air compliance program a revised notification at least seven days prior to the re-scheduled emissions test date or arrange a re-scheduled test date with the appropriate air compliance program by mutual agreement.

(10) Test Reports.

(a) The owner or owner’s authorized agent of an emissions unit for which an emissions test is required shall submit a written test report to the compliance authority specified by permit, on the results of each such test as soon as practicable but no later than 45 days after the last run of each test is completed. Test reports may be submitted electronically.

(b) If the owner or owner’s authorized agent of an emissions unit for which an emissions test is required submits the results of each such test electronically using the EPA Electronic Reporting Tool (ERT), the written report specified in paragraph 62-297.310(10)(a), F.A.C., need not be submitted, provided the conditions of subparagraphs 62-297.310(10)(b)1. through 3., F.A.C., are met:

1. The owner or owner’s authorized agent shall submit the test information using the ERT as soon as practicable but no later than 45 days after the last run of each test is completed,

2. The test information shall provide, as a minimum, the information specified in subparagraphs 62-297.310(10)(c)1. through 24., F.A.C.; and,

3. The compliance authority specified by permit must receive written notification, no later than 45 days after the last run of each test is completed, of the date that the test data was submitted using the ERT.

(c) The test report shall provide sufficient detail on the emissions unit tested and the test procedures used to allow the Department to determine if the test was properly conducted and the test results properly computed. As a minimum, the test report, other than for an EPA Method 9 test, shall provide the following information:

1. The type, location, and identification number of the emissions unit tested.

2. The facility at which the emissions unit is located.

3. The owner and, if other than the owner, operator of the emissions unit.

4. The type and amount of fuels and materials typically used and processed, and the actual types and amounts of fuels used and material processed during each test run.

5. If necessary in order to compare the emissions test results with an applicable emission limiting standard, the means, raw data, and computations used to determine the amount of fuels used and materials processed.

6. The type of air pollution control devices installed on the emissions unit, their general condition, their typical operating parameters, and their actual operating parameters during each test run.

7. A diagram of the sampling location, including the distance to any upstream and downstream bends or other flow disturbances.

8. The date, starting time, and duration of each sampling run.

9. The test procedures, including any authorized alternative procedures, used.

10. The number of points sampled, and the configuration and location of the sampling plane.

11. For each sampling point for each run, the dry gas meter reading, velocity head, pressure drop across the stack or duct, temperatures, average meter temperatures, and sample time per point.

12. The type, manufacturer, and configuration of the sampling equipment used.

13. Data related to the required calibration of the test equipment.

14. Data on the identification, processing, and weights of all filters used.

15. Data on the types and amounts of any chemical solutions used.

16. For each sampling run, data on the amount of pollutant collected from each sampling probe.

17. For each sampling run, data on the amount of pollutant collected from the filters.

18. For each sampling run, data on the amount of pollutant collected from the impingers.

19. The names of individuals who furnished the process variable data, conducted the test, analyzed the samples and prepared the report.

20. All measured and calculated data required to be determined by each applicable test procedure for each run.

21. The detailed calculations for one run that relate the collected data to the calculated emission rate or concentration, as applicable.

22. The applicable emission standard, and the resulting maximum allowable emission rate or concentration for the emissions unit, as applicable, plus the test result in the same form and unit of measure.

23. When an emissions test is conducted for the Department or its agent, the person who conducts the test shall provide the certification with respect to the test procedures used. The owner or owner’s authorized agent shall certify that all data required and provided to the person conducting the test are true and correct to his or her knowledge.

24. For non-Title V sources, a certification by the owner or owner’s authorized agent that, to his or her knowledge, all data submitted are true and correct.

25. Any report submitted for a Title V source shall contain certification by a responsible official. This certification shall state that, based on information and belief formed after reasonable inquiry, the statements and information in the document are true, accurate, and complete.

Rulemaking Authority 403.061 FS. Law Implemented 403.031, 403.061, 403.087, 403.0872 FS. History–Formerly 17-2.700(1)(b), 17-297.310, Amended 11-23-94, 3-13-96, 10-28-97, 3-2-99, 3-9-15.

## 62-297.320 Standards for Persons Engaged in Visible Emissions Observations.

(1) Training and Certification Required. All persons engaged in determining the opacity of visible emissions in Florida shall attend training and be certified by a training provider in accordance with the procedures and requirements set forth below.

(a) Certification shall consist of satisfactory attendance and completion of a classroom lecture and a field qualification. For certification purposes, the classroom lecture and field qualification are separate and independent requirements.

(b) Attendance at the classroom lecture is required no less frequently than every three years. Successful completion of the field qualification is required no less frequently than every six months.

(c) Proof of certification shall be made by including copies of the signed and dated certificates or cards issued by the training providers with documentation of visible emissions observations submitted to the department, or otherwise upon request of the department.

(2) Requirements for Training Providers. All persons providing training leading to the certification of persons engaged in determining the opacity of visible emissions in Florida shall meet the requirements of subsections 62-297.320(2)-(8), F.A.C.

(a) For certification purposes, the classroom lecture and field certification are separate and independent requirements. For each course scheduled, each training provider shall offer a classroom lecture and one or more days of field qualification.

(b) Copies of quality assurance documentation, attendance records and field data sheets shall be maintained for a period of no less than three years after the conclusion of each course and shall be made available to the department upon request.

(c) Each training provider shall arrange for suitable locations for the classroom lecture and field qualification sessions that facilitate learning and reduce the impact of the smoke on passersby.

(d) To assure that cigar, pipe or cigarette smoke does not interfere with the observations of the trainees, each training provider shall enforce a policy of no smoking within the field qualification area.

(3) Classroom Lecture.

(a) The classroom lecture shall include the following topics and exercises:

1. Sources and causes of visible emissions.

2. Common types of emission control equipment and their effects on visible emissions observations.

3. History of opacity measurement.

4. Principles and theory of opacity.

5. Plume types and characteristics.

6. Legal aspects of visible emissions observations and legal defensibility of Method 9.

7. Basic meteorological conditions that influence plume behavior.

8. Proper procedures for conducting field observations under a variety of conditions.

9. A demonstration of commonly used measurement devices including a compass, a wind speed measurement device, and an inclinometer.

10. A written exercise demonstrating the proper procedure for documentation of observations.

(b) Training providers shall issue a signed and dated certificate or card to all persons attending the classroom lecture.

(4) Field Qualification.

(a) The field qualification shall be conducted in accordance with the requirements set forth in 40 CFR Part 60, Subpart A, EPA Method 9, adopted and incorporated by reference at Rule 62-204.800, F.A.C.; EPA Quality Assurance Handbook for Air Pollution Measurement Systems: Volume III, Section 3.12, hereby adopted and incorporated by reference; and EPA Guidelines for Evaluation of Visible Emissions (EPA 340/1-75-007, April 1975), hereby adopted and incorporated by reference.

(b) Each training provider shall meet requirements for quality assurance at least as stringent as those outlined in EPA Method 9.

(c) Each training provider shall monitor the attendees so that conferring or copying results during field qualification does not occur.

(d) Each training provider shall not provide hints of any kind or demonstrate the smoke standards during the field qualification sessions, except during familiarization runs prior to each test.

(e) Training providers shall issue a signed and dated certificate or card to all persons who successfully complete the field qualification.

(5) Notification to Department of Training Course Offerings. Each training provider shall notify the department of all visible emissions training courses such provider offers in Florida at least 30 days prior to the start of each course.

(6) Notification to Department of Persons Receiving Certification. Each training provider shall provide a list of the names of attendees receiving certification at its courses to the department no later than 30 days after the conclusion of each course.

(7) Audit by the Department. For auditing purposes, each training provider shall allow one or more persons from the department or a local air pollution control agency to observe each visible emissions training course offered in Florida without advance notice to the training provider. The training provider shall not issue a certificate or card to the observers, and shall not charge a fee for their attendance.

(8) Invalidation of Certificates. After investigation by the department, should any training provider’s course be found by the department to not meet the requirements of this section, the certificates or cards offered by such provider for such course shall not be considered valid for visible emissions observations in Florida.

Rulemaking Authority 403.061 FS. Law Implemented 403.031, 403.061 FS. History–New 2-12-04.

## 62-297.401 Compliance Test Methods.

Rulemaking Authority 403.061 FS. Law Implemented 403.031, 403.061, 403.087 FS. History–Formerly 17-2.700(6)(b), Amended 6-11-93, Formerly 17-297.401, Amended 11-23-94, 1-1-96, 3-13-96, 10-7-96, 3-2-99, Repealed 7-10-14.

## 62-297.440 Supplementary Test Procedures.

The following test procedures are adopted by reference. Copies of these documents are available from the sources set forth below. Copies may also be inspected at the Department’s Tallahassee Office.

(1) [Reserved].

(2) EPA Reports – EPA occasionally publishes test methods and emission control guidelines in a report format. These documents are available (unless otherwise stated) from the National Technical Information Services, 5286 Port Royal Road, Springfield, Virginia 22216, and may be inspected at the Department’s Tallahassee Office.

(a) Petroleum Liquid Storage.

1. Control of Volatile Organic Emissions from Petroleum Liquid Storage in External Floating Roof Tanks, EPA 450/2-78-047, p. 5-3.

2. Control of Volatile Organic Emissions from Storage of Petroleum Liquids in Fixed-Roof Tanks, EPA 450/2-77-036, p. 6-2.

(b) Gasoline Bulk Terminals.

1. Vapor Control System Test.

a. VOC emissions from the vapor control system shall be determined by the method given in Appendix A of EPA 450/2-77-026, except that an adequate sampling time shall be at least six (6) hours of operation. For continuous vapor processing systems at least 80,000 gallons (302,800 liters) of gasoline shall be loaded during the test. For intermittent vapor processing systems, at least 80,000 gallons (302,800 liters) of gasoline shall be loaded during the test and at least two full cycles of operation of the vapor processing system shall occur. This test shall be performed prior to the date of compliance and annually thereafter. Test results records shall be maintained at the terminal until the subsequent annual test shall be made available to the department upon request.

b. Control of Hydrocarbons from Tank Truck Gasoline Loading Terminals, EPA 450/2-77-026, Appendix A. Emission Test Procedure for Tank Truck Gasoline Loading Terminals.

2. Vapor Leak Detection.

a. During loading or unloading operations at bulk terminals, there shall be no reading greater than or equal to 100 percent of the lower explosive level (LEL), measured as propane at 1 in. (2.5 centimeters) around the perimeter of a potential leak source as detected by a combustible gas detector using the procedure described in Appendix B of EPA 450/2-78-051.

b. Control of Volatile Organic Compound Leaks from Gasoline Tank Trucks and Vapor Collection Systems, EPA 450/2-78-051, Appendix B, Gasoline Vapor Leak Detection Procedures by Combustible Gas Detector.

(c) Gasoline Service Stations.

1. Design Criteria for Stage I Vapor Control: Gasoline Service Stations, USEPA, OAQPS, ESED, November, 1975.

2. [Reserved].

(d) Non-destructive Control Devices.

1. Measurement of Volatile Organic Compounds, EPA 450/2-78-041, Attachment 3, Alternate Test for Direct Measurement of Total Gaseous Organic Compounds Using a Flame Ionization Analyzer.

2. [Reserved].

(e) Perchloroethylene Dry Cleaning Systems.

1. Control of Volatile Organic Emissions from Perchloroethylene Dry Cleaning Systems, EPA 450/2-78-050, p. 6-3, Compliance Procedures, Liquid Leakage.

2. RACT Compliance Guidance for Carbon Absorbers on Perchloroethylene Dry Cleaners. Task No. 119, Contract No. 68-01-4147. EPA, DSSE, May, 1980, pp. 8 – 21, Appendices A and B.

(f) Cross Recovery Determination. When determining if a kraft recovery furnace is a straight kraft or cross recovery furnace the procedure in 40 CFR 60.285(d)(3) of Subpart BB shall be used.

(3) [Reserved].

(4) American Petroleum Institute (API) Recommended Practices – These are available from the API, 2101 L Street, Northwest, Washington, D.C. 20037

(a) API Standard 650, Welded Steel Tanks for Oil Storage, Sixth Edition, Revision 1, May 15, 1978.

(b) API Publication 2517, Evaporation Loss from External Floating Roof Tanks, Second Edition, February, 1980.

(c) API 1004, Bottom Loading and Vapor Recovery for MC-306 Tank Motor Vehicles, Fourth Edition, September 1, 1977.

Rulemaking Authority 403.061 FS. Law Implemented 403.031, 403.061, 403.087 FS. History–Formerly 17-2.700(6)(c), Amended 6-11-93, Formerly 17-297.440, Amended 11-23-94, 1-1-96, 3-2-99, 10-22-02, 7-10-14.

## 62-297.450 EPA VOC Capture Efficiency Test Procedures.

(1) Applicability. The requirements set forth in subsections 62-297.450(2) and (3), F.A.C., shall apply to all regulated VOC-emitting emissions units employing a control system pursuant to Rules 62-296.501 through 62-296.516, and 62-296.800, F.A.C.

(2) Capture Efficiency Determination. The owner or operator shall determine the capture efficiency of a VOC capture system by using the EPA Emission Measurement Technical Information Center Guideline Document GD-035, “Guidelines for Determining Capture Efficiency,” January 9, 1995 (http://www.flrules.org/Gateway/reference.asp?No=Ref-04299), hereby adopted and incorporated by reference; and one or more of the following EPA test methods, adopted and incorporated by reference at Rule 62-204.800, F.A.C., as applicable to the capture system:

(a) Method 204, Criteria for and Verification of a Permanent or Temporary Total Enclosure;

(b) Method 204A, Volatile Organic Compounds Content in Liquid Input Stream;

(c) Method 204B, Volatile Organic Compounds Emissions in Captured Stream;

(d) Method 204C, Volatile Organic Compounds Emissions in Captured Stream, (Dilution Technique);

(e) Method 204D, Volatile Organic Compounds Emissions in Uncaptured Stream from Temporary Total Enclosure;

(f) Method 204E, Volatile Organic Compounds Emissions in Uncaptured Stream from Building Enclosure, or

(g) Method 204F, Volatile Organic Compounds Content in Liquid Input Stream (Distillation Approach).

(3) In lieu of determining the capture efficiency of a capture system, the owner or operator of an affected activity, process, or emissions unit may determine the overall emission reduction efficiency of the system by dividing the recovered liquid VOC by the input liquid VOC using the procedure given in 40 C.F.R. §60.433, adopted and incorporated by reference at Rule 62-204.800, F.A.C., if all of the following criteria are met:

(a) The owner or operator uses a nondestructive control device designed to collect and recover VOC; and,

(b) The owner or operator is able to equate solvent usage with solvent recovery on a 24-hour (daily) basis, rather than a 20-day weighted average; and,

(c) The owner or operator can equate solvent usage with solvent recovery within 72 hours following each 24-hour period; and,

(d) The solvent recovery system (i.e., capture and control system) is dedicated to a single activity, process line, or emissions unit; or the solvent recovery system controls multiple activities, process lines, or emissions units, and the owner or operator is able to demonstrate that the overall control (i.e., the total recovered solvent VOC divided by the sum of liquid VOC input to all activities, process lines, or emissions units venting of the control system) meets or exceeds the most stringent emission standard applicable for any activity, process line, or emissions unit venting to the control system.

(4) Recordkeeping and Reporting.

(a) The owner or operator of an affected activity, process, or emissions unit shall submit to the department a list of the procedures that will be used for the capture efficiency tests at the owner or operator’s facility. A copy of the list shall be kept on file at the affected facility.

(b) Required test reports shall be submitted to the department within forty-five (45) days of the test date. A copy of the results shall be kept on file at the facility.

(c) If any physical or operational change is made to a control system, the owner or operator of the affected facility shall notify the department of the change within ten (10) working days after making such change. The department shall require the owner or operator of the affected activity, process, or emissions unit to conduct a new capture efficiency test if the department has reason to believe (based on engineering calculations or empirical evidence) that a physical or operational change made to the capture system has decreased the overall emissions reduction efficiency of the system.

(d) The owner or operator of an affected activity, process, or emissions unit shall notify the department thirty (30) days prior to performing any capture efficiency and/or control efficiency tests.

(e) The owner or operator of an affected activity, process, or emissions unit using a Permanent Total Enclosure shall demonstrate that this enclosure meets the requirement given in Method 204 for a Permanent Total Enclosure during any required control device efficiency test.

(f) The owner or operator of an affected activity, process, or emissions unit using a Temporary Total Enclosure shall demonstrate that this enclosure meets the requirements given in Method 204 for a Temporary Total Enclosure during any required control device efficiency test.

Rulemaking Authority 403.061 FS. Law Implemented 403.031, 403.061, 403.087 FS. History–Formerly 17-2.700(7), Amended 6-11-93, Formerly 17-297.450, Amended 11-23-94, 1-1-96, 3-2-99, 7-10-14.

## 62-297.520 EPA Continuous Monitor Performance Specifications.

Rulemaking Authority 403.061 FS. Law Implemented 403.031, 403.061, 403.087 FS. History–New 6-29-93, Formerly 17-297.520, Amended 11-23-94, 3-13-96, 3-2-99, Repealed 2-16-12.

## 62-297.620 Exceptions and Approval of Alternate Procedures and Requirements.

(1) The owner or operator of any emissions unit subject to the provisions of this chapter may request in writing a determination by the Secretary or his/her designee that any requirement of this chapter (except for any continuous monitoring requirements) relating to emissions test procedures, methodology, equipment, or test facilities shall not apply to such emissions unit, and shall request approval of an alternate procedure or requirement.

(2) The request shall set forth the following information, at a minimum:

(a) Specific emissions unit and permit number, if any, for which exception is requested.

(b) The specific provision(s) of this chapter from which an exception is sought.

(c) The basis for the exception, including but not limited to any hardship which would result from compliance with the provisions of this chapter.

(d) The alternate procedure(s) or requirement(s) for which approval is sought and a demonstration that such alternate procedure(s) or requirement(s) shall be adequate to demonstrate compliance with applicable emission limiting standards contained in the rules of the department or any permit issued pursuant to those rules.

(3) The Secretary or his/her designee shall specify by order each alternate procedure or requirement approved for an individual emissions unit in accordance with this section or shall issue an order denying the request for such approval. The department’s order shall be final agency action, reviewable in accordance with Section 120.57, F.S.

(4) In the case of an emissions unit which has the potential to emit less than 100 tons per year of particulate matter and is equipped with a baghouse, the Secretary or the appropriate Director of District Management may waive any particulate matter compliance test requirements for such emissions unit specified in any otherwise applicable rule, and specify an alternative standard of 5% opacity. The waiver of compliance test requirements for a particulate emissions unit equipped with a baghouse, and the substitution of the visible emissions standard, shall be specified in the permit issued to the emissions unit. If the department has reason to believe that the particulate weight emission standard applicable to such an emissions unit is not being met, it shall require that compliance be demonstrated by the test method specified in the applicable rule.

Rulemaking Authority 403.061 FS. Law Implemented 403.021, 403.031, 403.061, 403.087 FS. History–Formerly 17-2.700(3), Amended 6-11-93, Formerly 17-297.620, Amended 11-23-94.