62-348.200 Definitions.

The definitions in Sections 373.019, 373.403, 378.403, 403.031 and 403.803, F.S., and the following definitions apply to this chapter:

(1) “Herbaceous freshwater wetlands” means wetlands where less than 10 percent of the vegetation is woody vegetation and the chloride concentration meets the definition of predominately freshwaters as defined in Rule 62-302.200, F.A.C. Such areas are typically known as marshes, but may include other forms of wetlands dominated by herbaceous freshwater vegetation.

(2) “High-quality peat” means peat from a herbaceous freshwater wetland that is classified as H1 to H4 on the von Post Humification Scale and has a pH less than 7. The following method, incorporated herein by reference, shall be used to determine the classification on the von Post Humification Scale, for use in this chapter: American Society for Testing and Materials, D5715-00 (Reapproved 2006) Standard Test Method for Estimating the Degree of Humification of Peat and Other Organic Soils (Visual/Manual Method), Volume 04.08, Issued March 2000. This document may be reviewed at the Florida Department of Environmental Protection, 2600 Blair Stone Road, Mail Station 3577, Tallahassee, Florida 32399-2400, or a copy obtained from the American Society for Testing and Materials, 100 Barr Harbor Drive, Post Office Box C700, West Conshohocken, Pennsylvania 19428-2959. The following method, incorporated herein by reference, shall be used to determine the pH for use in this chapter: U.S. Environmental Protection Agency, EPA 150.1, Methods for the Chemical Analysis of Water and Waste, EPA-600/4-79-020, Revised 1983. A copy of this document may be obtained by writing to the Florida Department of Environmental Protection, 2600 Blair Stone Road, Mail Station 3577, Tallahassee, Florida 32399-2400.

(3) “High-quality peat extraction area” or “extraction area” means an area of herbaceous freshwater wetland, or an area of historically herbaceous freshwater wetland, where cumulatively no less than 80 percent of the extracted peat is high-quality peat.

(4) “Historically herbaceous freshwater wetlands” means wetlands that, as determined using aerial photography, would meet the definition of herbaceous freshwater wetlands if not for human alteration of environmental conditions.

(5) “Horticultural industry” means the industry that cultivates plants in Florida, such as, trees, shrubs, flowers, annuals, perennials, tropical foliage, liners, ferns, vines, bulbs, grafts, scions, or buds, but not turf grasses. The plants are grown or kept for propagation or distribution for retail, wholesale, or re-wholesale purposes.

(6) “Invasive Exotic” for purposes of this rule means those plant species listed in the Florida Exotic Pest Plant Council’s 2009 List of Invasive Species Category I and II, which is incorporated herein by reference. A copy of this document may be obtained from the Department in the manner described in Rule 62-348.900, F.A.C.

(7) “Larger plan of development” means a common plan of development or sale that includes:

(a) Any activity initiated by the surveying, planning, or platting of contiguous real property, where such activity facilitates the advancement of a common type of land use (such as multiple residences, a residential subdivision, or phased site development) on the subject property, or

(b) Any activity on contiguous real property that comprises a total land area divided into three or more lots, parcels, tracts, tiers, blocks, sites, or units, and is served by a common road or road network or common surface water management system within that land area. Areas of land that are divided by public or private roads are considered contiguous if such areas are under one ownership or control.

(8) “Nuisance Species” shall mean plant species as defined in Rule 62-302.200, F.A.C.

(9) “Open water” means an area of surface waters as identified by Rule 62-340.600, F.A.C., which under normal circumstances does not support emergent vegetation.  For the purpose of this definition, emergent vegetation does not include aquatic vegetation as defined in Rule 62-340.200, F.A.C.

(10) “Recycled materials” means those materials that are capable of being recycled and that would otherwise be processed or disposed of as solid waste.

(11) “Registered Professional” means a professional registered or licensed in Florida with the necessary expertise in the fields of hydrology, hydrogeology, hydraulics, drainage, flood control, erosion and sediment control, and stormwater pollution control, and who is qualified by education and experience in the technical analyses, design, and application of required structures, processes, and systems, to design and certify the stormwater management systems under review. Examples of registered professionals, authorized pursuant to Chapter 455, F.S., and the respective practice acts by which they are regulated, are professional engineers licensed under Chapter 471, F.S., professional landscape architects licensed under Chapter 481, F.S., professional surveyors and mappers licensed under Chapter 472, F.S., and professional geologists licensed under Chapter 492, F.S. Registered professionals may sign and seal only those drawings, documents, and calculations commensurate with their skills, background, knowledge, education, and experience, and in accordance with their respective practice acts.

(12) “Renewable materials” means those materials that are able to be sustained indefinitely because of inexhaustible supplies or new growth.

Rulemaking Authority 373.026(7), 373.043, 373.414, 373.4145, 373.418, 373.421, 403.805(1) FS. Law Implemented 373.019, 373.403, 373.413, 373.414, 373.4145, 373.416, 373.421, 373.4211, 373.426, 378.403, 403.031, 403.803 FS. History–New 8-18-10.