25-4.071 Adequacy of Service.

(1) Each telecommunications company shall provide switching equipment, trunking, and associated facilities within its operating territory for the handling of local and toll traffic, designed and engineered on the basis of realistic forecasts of growth so that during the average busy season busy hour at least 97 percent of all calls offered to any trunk group (toll connecting, inter-office, extended area service) shall not encounter an all-trunk busy condition.

(2) Telephone calls to valid numbers should encounter a ring-back tone, line busy signal, or non-working number intercept facility (operator or recording) after completion of dialing. The call completion standards established for such calls by category of call is as follows:

(a) Intra-office Calls – 95 percent,

(b) Inter-office Calls – 95 percent,

(c) Extended Area Calls – 95 percent, and

(d) Intra-LATA DDD Calls – 95 percent.

(3) All telephone calls to invalid telephone numbers shall encounter an operator or suitable recorded intercept facility, preferably a recording other than the non-working number recording used for valid number calls.

(4) Intercept service shall be as outlined in Rule 25-4.074, F.A.C.

(5) A line busy signal (60 impulse per minute tone) shall not be used for any signaling purpose except to denote that a subscriber’s line, other valid terminal, centrex or PBX trunks, or equipment where the quantity is controlled by the customer is in use.

Specific Authority 350.127(2) FS. Law Implemented 364.01(4), 364.03, 364.15, 364.17, 364.18, 364.183, 364.19, 364.386 FS. History–Revised 12-1-68, Amended 3-31-76, Formerly 25-4.71, Amended 6-24-90, 3-10-96.