61G15-34.004 Design of Process and Fluid Flow Systems.

(1) Process and Fluid Flow Systems are those systems that are designed to move fluids either by pumps, fans, or gravity as part of an industrial, commercial, or cogeneration process. Items to be included in the design of these systems are fluid type and characteristics, fluid flow quantities, fluid pressure head, pump type, fan type, piping specifications, ductwork, specifications and process type.

(2) Mechanical documents applicable to fluid flow systems shall at a minimum include the following:

(a) Equipment schedule for each piece of mechanical equipment including fluid type and characteristics, system pressure head and flow requirements, and electrical or fuel requirements.

(b) Floor plans, site plans, and building and system elevations.

(c) Process flow diagrams with pipe or ductwork layout.

(d) System piping or ductwork layout.

(e) Specific system design requirements to allow for independent project review.

(f) List of NFPA, ASHRAE, ASME, ANSI or other applicable design standards and requirements.

(g) Instrumentation and Control Diagrams and sequence of operation.

(h) Required fire protection systems and devices.

Specific Authority 471.008, 471.033(2) FS. Law Implemented 471.033 FS. History–New 11-16-94.