61G15-34.006 Design of Material and Human Transfer Systems.

(1) Material and Human Transfer Systems are those systems that are designed to move materials or humans from one place to another as a part of an industrial or commercial process.

(2) Mechanical documents applicable to material and human transfer systems shall at a minimum include the following:

(a) Equipment schedule items to be included in the design of these systems are material type and characteristics, material flow quantities, material or human weight, conveyor types, elevator types, electrical and hydraulic requirements, and ventilation requirements.

(b) Floor plans, site plans, and building and system elevations.

(c) Process flow diagrams with appropriate system sizing information.

(d) System conveyor and/or elevator layout.

(e) Specific system design requirements to allow for independent project review.

(f) List of NFPA, ASHRAE, ASME or other applicable design codes, standards, and requirements.

(g) Instrumentation and Control Diagrams and sequence of operation.

(h) Required fire protection systems and devices.

Specific Authority 471.008, 471.033(2) FS. Law Implemented 471.033 FS. History–New 11-16-94.