62-210.300 Permits Required.

Unless exempted from permitting pursuant to paragraph 62-210.300(3)(a) or (b), F.A.C., or Rule 62-4.040, F.A.C., or unless specifically authorized by provision of subsection 62-210.300(4), F.A.C., or Rule 62-213.300, F.A.C., the owner or operator of any facility or emissions unit which emits or can reasonably be expected to emit any air pollutant shall obtain an appropriate permit from the Department prior to beginning construction, reconstruction pursuant to 40 CFR 60.15 or 63.2, modification, or the addition of pollution control equipment; or to authorize initial or continued operation of the emissions unit; or to establish a PAL or Air Emissions Bubble. All emissions limitations, controls, and other requirements imposed by such permits shall be at least as stringent as any applicable limitations and requirements contained in or enforceable under the State Implementation Plan (SIP) or that are otherwise federally enforceable. Issuance of a permit does not relieve the owner or operator of a facility or an emissions unit from complying with any applicable requirements, any emission limiting standards or other requirements of the air pollution rules of the Department or any other such requirements under federal, state, or local law.

(1) Air Construction Permits.

(a) Unless exempt from permitting pursuant to paragraph 62-210.300(3)(a) or (b), F.A.C., or Rule 62-4.040, F.A.C., an air construction permit shall be obtained by the owner or operator of any proposed new, reconstructed, or modified facility or emissions unit, or any new pollution control equipment prior to the beginning of construction, reconstruction pursuant to 40 CFR 60.15 or 63.2, or modification of the facility or emissions unit or addition of the air pollution control equipment; or to establish a PAL; in accordance with all applicable provisions of this chapter, Chapter 62-212, F.A.C., and Chapter 62-4, F.A.C. Except as provided under Rule 62-213.415, F.A.C., the owner or operator of any facility seeking to create or change an air emissions bubble shall obtain an air construction permit in accordance with all the applicable provisions of this chapter, Chapters 62-212 and 62-4, F.A.C. The construction permit shall be issued for a period of time sufficient to allow construction, reconstruction or modification of the facility or emissions unit or addition of the air pollution control equipment; and operation while the owner or operator of the new, reconstructed or modified facility or emissions unit or the new pollution control equipment is conducting tests or otherwise demonstrating initial compliance with the conditions of the construction permit.

(b) Notwithstanding the expiration of an air construction permit, all limitations and requirements of such permit that are applicable to the design and operation of the permitted facility or emissions unit shall remain in effect until the facility or emissions unit is permanently shut down, except for any such limitation or requirement that is obsolete by its nature (such as a requirement for initial compliance testing) or any such limitation or requirement that is changed in accordance with the provisions of subparagraph 62-210.300(1)(b)1., F.A.C. Either the applicant or the Department can propose that certain conditions be considered obsolete. Any conditions or language in an air construction permit that are included for informational purposes only, if they are transferred to the air operation permit, shall be transferred for informational purposes only and shall not become enforceable conditions unless voluntarily agreed to by the permittee or otherwise required under Department rules.

1. Except for those limitations or requirements that are obsolete, all limitations and requirements of an air construction permit shall be included and identified in any air operation permit for the facility or emissions unit. The limitations and requirements included in the air operation permit can be changed, and thereby superseded, through the issuance of an air construction permit, federally enforceable state air operation permit, federally enforceable air general permit, or Title V air operation permit; provided, however, that:

a. Any change that would constitute an administrative correction may be made pursuant to Rule 62-210.360, F.A.C.;

b. Any change that would constitute a modification, as defined at Rule 62-210.200, F.A.C., shall be accomplished only through the issuance of an air construction permit; and

c. Any change in a permit limitation or requirement that originates from a permit issued pursuant to 40 C.F.R. 52.21, subparagraph 62-204.800(10)(d)2., F.A.C., Rule 62-212.400, F.A.C., Rule 62-212.500, F.A.C., or any former codification of Rule 62-212.400 or 62-212.500, F.A.C., shall be accomplished only through the issuance of a new or revised air construction permit under subparagraph 62-204.800(10)(d)2., F.A.C., Rule 62-212.400 or 62-212.500, F.A.C., as appropriate.

2. The force and effect of any change in a permit limitation or requirement made in accordance with the provisions of subparagraph 62-210.300(1)(b)1., F.A.C., shall be the same as if such change were made to the original air construction permit.

3. Nothing in paragraph 62-210.300(1)(b), F.A.C., shall be construed as to allow operation of a facility or emissions unit without a valid air operation permit.

(2) Air Operation Permits. Upon expiration of the air operation permit for any existing facility or emissions unit, subsequent to construction or modification, or subsequent to the creation of or change to a bubble, and demonstration of compliance with the conditions of the construction permit for any new or modified facility or emissions unit, any air emissions bubble, or as otherwise provided in this chapter or Chapter 62-213, F.A.C., the owner or operator of such facility or emissions unit shall obtain a renewal air operation permit, an initial air operation permit or air general permit, or an administrative correction or revision of an existing air operation permit, whichever is appropriate, in accordance with all applicable provisions of this chapter, Chapter 62-213 (if the facility is a Title V source), and Chapter 62-4, F.A.C.

(a) Minimum Requirements for All Air Operation Permits. At a minimum, a permit issued pursuant to this subsection shall:

1. Specify the manner, nature, volume and frequency of the emissions permitted, and the applicable emission limiting standards or performance standards, if any;

2. Require proper operation and maintenance of any pollution control equipment by qualified personnel, where applicable in accordance with the provisions of any operation and maintenance plan required by the air pollution rules of the Department.

3. Contain an effective date stated in the permit which shall not be earlier than the date final action is taken on the application and be issued for a period, beginning on the effective date, as provided below.

a. The operation permit for an emissions unit which is in compliance with all applicable rules and in operational condition, and which the owner or operator intends to continue operating, shall be issued or renewed for a five-year period, except that, for Title V sources subject to subparagraph 62-213.420(1)(a)1., F.A.C., operation permits shall be extended until 60 days after the due date for submittal of the facility’s Title V permit application as specified in subparagraph 62-213.420(1)(a)1., F.A.C.

b. Except as provided in sub-subparagraph 62-210.300(2)(a)3.d., F.A.C., the operation permit for an emissions unit which has been shut down for six months or more prior to the expiration date of the current operation permit, shall be renewed for a period not to exceed five years from the date of shutdown, even if the emissions unit is not maintained in operational condition, provided:

(I) The owner or operator of the emissions unit demonstrates to the Department that the emissions unit may need to be reactivated and used, or that it is the owner’s or operator’s intent to apply to the Department for a permit to construct a new emissions unit at the facility before the end of the extension period; and

(II) The owner or operator of the emissions unit agrees to and is legally prohibited from providing the allowable emission permitted by the renewed permit as an emissions offset to any other person under Rule 62-212.500, F.A.C.; and

(III) The emissions unit was operating in compliance with all applicable rules as of the time the source was shut down.

c. Except as provided in sub-subparagraph 62-210.300(2)(a)3.d., F.A.C., the operation permit for an emissions unit which has been shut down for five years or more prior to the expiration date of the current operation permit shall be renewed for a maximum period not to exceed ten years from the date of shutdown, even if the emissions unit is not maintained in operational condition, provided the conditions given in sub-subparagraph 62-210.300(2)(a)3.b., F.A.C., are met and the owner or operator demonstrates to the Department that failure to renew the permit would constitute a hardship, which may include economic hardship.

d. The operation permit for an electric utility generating unit on cold standby or long-term reserve shutdown shall be renewed for a five-year period, and additional five-year periods, even if the unit is not maintained in operational condition, provided the conditions given in sub-sub-subparagraphs 62-210.300(2)(a)3.b.i. through iii., F.A.C., are met.

4. In the case of an emissions unit permitted pursuant to sub-subparagraphs 62-210.300(2)(a)3.b., c., and d., F.A.C., include reasonable notification and compliance testing requirements for reactivation of such emissions unit and provide that the owner or operator demonstrate to the Department prior to reactivation that such reactivation would not constitute reconstruction pursuant to subsection 62-204.800(7), F.A.C.

(b) Additional Requirements for Federally Enforceable State Operation Permits (FESOPs) for Non-Title V Sources.

1. An operation permit for a non-Title V source, including a synthetic non-Title V source, shall be considered federally enforceable only if it is issued, renewed, or revised in accordance with the following provisions:

a. At the time of initial application for the permit, the applicant requests that the permit be made federally enforceable.

b. A notice of proposed agency action on the initial application, any renewal application involving material changes from the existing permit, and any application for permit revision is published in accordance with the provisions of subsections 62-210.350(1) and (4), F.A.C., except as provided in subparagraph 62-210.300(2)(b)3., F.A.C.

c. The permit is a facility-wide permit.

d. The permit is conditioned such that the owner or operator is legally obligated to adhere to the terms and limitations of such permit, including any condition or limitation assumed by the owner or operator upon acceptance of such permit.

e. The permit is conditioned such that any emissions limitation, control requirement, or other requirement assumed by the owner or operator upon acceptance of such permit shall be quantifiable and enforceable as a practical matter.

2. Once a synthetic non-Title V source has been issued a federally enforceable state operation permit (FESOP), it shall remain subject to the requirements of paragraph 62-210.300(2)(b), F.A.C., unless:

a. The owner or operator accepts a higher limit and the facility becomes a Title V source; or

b. The owner or operator demonstrates to the Department that it no longer needs a federally enforceable operation permit to be classified as a non-Title V source (i.e., the facility is naturally “minor” without any federally enforceable limits) and specifically requests exemption from these requirements.

3. If all of the permitted emissions units within a facility have been issued one or more air construction permits which have undergone public notice in accordance with procedures at least as stringent as those provided in subsection 62-210.350(4), F.A.C., and the applicant requests that the conditions of such construction permit(s) be transferred without material change to a federally enforceable state operation permit (FESOP), the Department shall waive the requirements of sub-subparagraph 62-210.300(2)(b)1.b. and subparagraph 62-210.350(4)(a)3., F.A.C., for publication of a notice of proposed agency action; provided, however, that the remaining provisions of subsection 62-210.350(4), F.A.C., shall apply, including the requirement that notice be given to the U.S. Environmental Protection Agency and any local air pollution control program.

4. If an applicant requests that existing, multiple air operation permits for a facility be consolidated into a single federally enforceable state operation permit (FESOP), the Department shall reduce the permit processing fee required pursuant to Rule 62-4.050, F.A.C., by an amount equal to the sum of the processing fees paid for the existing permits prorated by the number of years remaining until expiration of each such permit.

(3) Exemptions. A facility, emissions unit or pollutant-emitting activity shall be exempt from the permitting requirements of this chapter, Chapters 62-212 and 62-4, F.A.C., if it satisfies the applicable criteria of paragraph 62-210.300(3)(a) or (b), F.A.C., or if it has been exempted from permitting pursuant to Rule 62-4.040, F.A.C. Failure of a facility, emissions unit or activity to satisfy the exemption criteria of paragraph 62-210.300(3)(a) or (b), F.A.C., does not preclude such facility, unit or activity from being considered for exemption pursuant to Rule 62-4.040, F.A.C. Emissions units and pollutant-emitting activities exempt from permitting under this rule shall not be exempt from the permitting requirements of Chapter 62-213, F.A.C., if they are contained within a Title V source; however, such emissions units and activities shall be considered insignificant for Title V purposes provided they also meet the criteria of subparagraph 62-213.300(2)(a)1. or paragraph 62-213.430(6)(b), F.A.C. Any proposed new emissions unit or activity that would be exempt from permitting under this rule shall not be required to obtain an air construction permit pursuant to this chapter, Chapter 62-212 or 62-4, F.A.C., even if such unit or activity would be contained within a Title V source. No emissions unit shall be entitled to an exemption from permitting under this rule if its emissions, in combination with the emissions of other units and activities at the facility, would cause the facility to emit or have the potential to emit any pollutant in such amount as to make the facility a Title V source. Neither shall any emissions unit be entitled to an exemption from permitting under this rule if it would be subject to any unit-specific applicable requirement including a PAL. Notwithstanding its exemption from air permitting, an exempt emissions unit or activity shall be subject to any general, facility-level applicable requirements, and its emissions shall be considered in determining the applicability of permitting requirements to other emissions units at the facility or to the facility as a whole.

(a) Categorical Exemptions.

1. One or more fossil fuel steam generators and hot water generating units located within a single facility; collectively having a total rated heat input equaling 100 million BTU per hour or less; and collectively burning annually no more than 145,000 gallons of fuel oil containing no more than 1.0 percent sulfur, or no more than 290,000 gallons of fuel oil containing no more than 0.5 percent sulfur, or an equivalent prorated amount of fuel oil if multiple fuels are used, provided none of the generators or hot water generating units is subject to the Federal Acid Rain Program or any standard or requirement under 42 U.S.C. section 7411 or 7412.

2. Any individual fossil fuel steam generator and hot water generating unit with a rated heat input equaling 100 million BTU per hour or less and burning annually no more than 150 million standard cubic feet of natural gas or no more than one million gallons of propane or no more than one million gallons of fuel oil containing no more than 0.05 percent sulfur, or an equivalent prorated amount if multiple fuels are used, provided:

a. The total annual fuel consumption for all units exempted by subparagraphs 62-210.300(3)(a)2. and 3., F.A.C., at a facility does not exceed 375 million standard cubic feet of natural gas or 2.5 million gallons of propane or 2.5 million gallons of fuel oil containing no more than 0.05 percent sulfur, or an equivalent prorated amount if multiple fuels are used and;

b. The unit is not subject to the Federal Acid Rain Program or any standard or requirement under 42 U.S.C. section 7411 or 7412.

3. One or more fossil fuel steam generators and hot water generating units located within a single facility, collectively having a total rated heat input equaling 10 million BTU per hour or less, and fired exclusively by natural gas or propane, provided:

a. During periods of natural gas curtailment, only propane or fuel oil containing no more than 1.0 percent sulfur is fired; and,

b. None of the generators or hot water heating units is subject to the Federal Acid Rain Program or any standard or requirement under 42 U.S.C. section 7411 or 7412.

4. Home heating and comfort heating with a gross maximum heat output of less than one million Btu per hour.

5. Internal combustion engines in boats, aircraft and vehicles used for transportation of passengers or freight.

6. Incinerators in one or two family dwellings or in multi-family dwellings containing four or less family units, one of which is owner-occupied.

7. Noncommercial and nonindustrial vacuum cleaning systems used exclusively for residential housekeeping purposes.

8. Cold storage refrigeration equipment, except for any such equipment located at a Title V source using an ozone-depleting substance regulated under 40 C.F.R. Part 82.

9. Vacuum pumps in laboratory operations.

10. Equipment used for steam cleaning.

11. Belt or drum sanders having a total sanding surface of five square feet or less and other equipment used exclusively on wood or plastics or their products having a density of 20 pounds per cubic foot or more.

12. Equipment used exclusively for space heating, other than boilers.

13. Noncommercial smoke houses used exclusively for smoking food products.

14. Bakery ovens located at any retail bakery facility which derives at least fifty percent of its revenues from retail sales on premises. Also, bakery ovens located at any commercial bakery facility utilizing only non-conveyor belt ovens operating on a single baking cycle in which a determinate amount of product is cooked at one baking (i.e., batch ovens).

15. Laboratory equipment used exclusively for chemical or physical analyses.

16. Brazing, soldering or welding equipment.

17. Laundry dryers, extractors, or tumblers for fabrics cleaned with only water solutions of bleach or detergents.

18. Petroleum dry cleaning facilities with a solvent consumption of less than 3,250 gallons per year.

19. Portable Air Curtain Incinerators. An air curtain incinerator shall be exempt from any requirement to obtain an air construction permit or non-Title V air operation permit provided it is constructed and operated in compliance with all of the following conditions.

a. Except as provided at sub-subparagraph 62-210.300(3)(a)19.c., F.A.C., only land clearing debris and appropriate starting fuel shall be burned in the air curtain incinerator. The air curtain incinerator shall not be used to burn any material prohibited to be open-burned as set forth at subsection 62-256.300(3), F.A.C. Only kerosene, diesel fuel, drip torch fuel (as used to ignite prescribed fires), untreated wood, virgin oil, natural gas or liquefied petroleum gas shall be used to start the fire in the air curtain incinerator. The use of used oil, chemicals, gasoline, or tires to start the fire is prohibited.

b. The air curtain incinerator, alone or in combination with any other air curtain incinerator(s) claiming this exemption from air permitting, shall not be deployed at a single site for more than six months in any 12-month period and, except as provided at sub-subparagraph 62-210.300(3)(a)19.c., F.A.C., shall not burn any material other than land clearing debris generated at the site or at any other site under control of the same person. For purposes of this rule, a site is any and all locations on one or more contiguous properties which are under the control of the same person (or persons under common control). Any deployment of one or more air curtain incinerators at a single site for more than six months in any 12-month period, and, except as provided at sub-subparagraph 62-210.300(3)(a)19.c., F.A.C., any use of an air curtain incinerator at a site to burn material other than land clearing debris generated at the site or any other site under control of the same person, shall require an appropriate air permit.

c. Notwithstanding the provisions of sub-subparagraphs 62-210.300(3)(a)19.a. and b., F.A.C., the air curtain incinerator may be used for up to six months in any 12-month period at any location for the destruction of animal carcasses in accordance with the provisions of subsection 62-256.700(6), F.A.C., the burning of storm-generated debris in accordance with the provisions of subsection 62-256.700(8), F.A.C., or the destruction of insect or disease-infested vegetation in accordance with the provisions of subsection 62-256.700(9), F.A.C. When using an air curtain incinerator to burn animal carcasses, untreated wood may also be burned to maintain good combustion.

d. If the air curtain incinerator employs an earthen trench, the pit walls (width and length) shall be vertical, and maintained as such, so that combustion of the waste within the pit is maintained at an adequate temperature and with sufficient air recirculation to provide enough residence time and mixing for proper combustion and control of emissions. Pit width shall not exceed twelve (12) feet.

e. Material shall not be loaded into the air curtain incinerator such that it protrudes above the level of the air curtain in the pit.

f. Ash shall not be allowed to build up in the pit of the air curtain incinerator to higher than 1/3 the pit depth or to the point where the ash begins to impede combustion, whichever occurs first.

g. In accordance with the provisions of 40 CFR Part 60, Subparts AAAA, BBBB, CCCC, and DDDD, adopted and incorporated by reference at Rule 62-204.800, F.A.C., visible emissions from the air curtain incinerator shall not exceed 10 percent opacity, six-minute average, except for up to 30 minutes during periods of startup, when visible emissions up to 35 percent opacity, six-minute average, shall be allowed. For purposes of this exemption, these visible emissions limitations shall not be considered unit-specific applicable requirements.

h. The air curtain incinerator shall be attended at all times while materials are being burned or flames are visible within the incinerator.

i. The air curtain incinerator shall be located at least 50 feet away from any wildlands, brush, combustible structure, or paved public roadway and 300 feet away from any occupied building.

j. If the air curtain incinerator is equipped with refractory-lined walls, charging shall begin no earlier than sunrise and must end no later than one hour after sunset. If the air curtain incinerator is not equipped with refractory-lined walls, charging shall begin no earlier than 8:00 a.m. Central time or 9:00 a.m. Eastern time and must end no later than one hour after sunset. After charging ceases, air flow shall be maintained until all material within the air curtain incinerator has been reduced to coals, and flames are no longer visible. A log shall be maintained onsite that documents daily beginning and ending times of charging.

k. Prior to any period of operation of the air curtain incinerator, the owner or operator shall contact the Division of Forestry regarding the planned burning activity.

l. If the owner of the air curtain incinerator, by lease or other means, grants authority to operate the incinerator to a person not in the employ of the owner, the owner shall provide such person with a copy of the conditions of this exemption.

m. If the air curtain incinerator is operated in compliance with all conditions of this exemption, it shall not be subject to any testing, reporting, or recordkeeping requirement for air curtain incinerators under 40 CFR Part 60, Subpart AAAA, BBBB, CCCC, or DDDD, adopted and incorporated by reference at Rule 62-204.800, F.A.C.; nor shall it be subject to the requirements of subsection 62-296.401(7), F.A.C.

20. One or more emergency generators located within a single facility provided:

a. None of the emergency generators is subject to the Federal Acid Rain Program; and

b. Total fuel consumption by all such emergency generators within the facility is limited to 32,000 gallons per year of diesel fuel, 4,000 gallons per year of gasoline, 4.4 million standard cubic feet per year of natural gas or propane, or an equivalent prorated amount if multiple fuels are used.

21. One or more heating units, general purpose internal combustion engines, or other combustion devices, all of which are located within a single facility, are not listed elsewhere in paragraph 62-210.300(3)(a), F.A.C., and are not pollution control devices, provided:

a. None of the heating units, general purpose internal combustion engines, or other combustion devices that would be exempted is subject to the Federal Acid Rain Program;

b. Total fuel consumption by all such heating units, general purpose internal combustion engines, and other combustion devices that would be exempted is limited to 32,000 gallons per year of diesel fuel, 4,000 gallons per year of gasoline, 4.4 million standard cubic feet per year of natural gas or propane, or an equivalent prorated amount if multiple fuels are used; and

c. Fuel for the heating units, general purpose internal combustion engines, and other combustion devices that would be exempted is limited to natural gas, diesel fuel, gasoline and propane.

22. Fire and safety equipment.

23. Surface coating operations within a single facility if the total quantity of coatings containing greater than 5.0 percent VOCs, by volume, used is 6.0 gallons per day or less, averaged monthly, provided:

a. Such operations are not subject to a volatile organic compound Reasonably Available Control Technology (RACT) requirement of Chapter 62-296, F.A.C.; and

b. The amount of coatings used shall include any solvents and thinners used in the process including those used for cleanup.

24. Surface coating operations utilizing only coatings containing 5.0 percent or less VOCs, by volume.

25. Phosphogypsum cooling ponds and inactive phosphogypsum stacks which have demonstrated compliance with the requirements of 40 C.F.R. Part 61, Subpart R, hereby adopted and incorporated by reference.

26. Degreasing units using heavier-than-air vapors exclusively, except any such unit using or emitting any substance classified as a hazardous air pollutant.

27. Volume reduction processes as defined in Rule 62-296.417, F.A.C., wherein the owner or operator manages only spent mercury-containing lamps removed from the facility where the volume reduction process is located.

28. Mercury recovery processes as defined in Rule 62-296.417, F.A.C., wherein the owner or operator manages only mercury-containing devices temporarily or permanently removed from service from the owner or operator’s own facilities or installations.

29. Bulk gasoline plants, provided:

a. Such operations are not conducted at a facility that is subject to the permitting requirements of Chapter 62-213, F.A.C., and the emissions from such operations would not contribute to total emissions that would make the facility subject to those requirements;

b. The facility receives and distributes only petroleum-based lubricants, gasoline, diesel fuel, mineral spirits and kerosene;

c. The total storage capacity for gasoline at the facility does not exceed 100,000 gallons;

d. The facility does not exceed a throughput rate (receive and distribute) of 1.3 million gallons of gasoline in any consecutive twelve-month period;

e. The facility is not subject to any Standard of Performance for New Stationary Sources (NSPS) requirement adopted by reference in Rule 62-204.800, F.A.C.; and

f. The facility is not subject to any volatile organic compound Reasonably Available Control Technology (RACT) requirement of Chapter 62-296, F.A.C.

30. Petroleum lubrication systems.

31. Application of fungicide, herbicide, or pesticide.

32. Asbestos renovation and demolition activities.

33. Non-halogenated solvent storage and cleaning operations, provided the solvents contain none of the hazardous air pollutants listed at Rule 62-210.200, F.A.C.

34. Vehicle refueling operations and associated fuel storage.

35. Restaurants.

36. Burning of drugs seized by law enforcement agencies in boilers with a heat input of 250 million BTU per hour or more.

37. Relocatable screening-only operations, provided:

a. The screening operation is not connected to a nonmetallic mineral processing plant subject to 40 CFR Part 60, Subpart OOO, adopted and incorporated by reference at Rule 62-204.800, F.A.C.;

b. No dry material is processed; and

c. No hazardous waste or toxic waste, as defined in Department rules, is processed.

38. Brownfield site remediation, as described at Rule 62-785.700, F.A.C., provided that the total volatile organic compounds in the air emissions from all onsite remediation equipment does not exceed 13.7 pounds per day.

(b) Generic and Temporary Exemptions.

1. Generic Emissions Unit Exemption. An emissions unit or pollutant-emitting activity that is not entitled to a categorical exemption pursuant to paragraph 62-210.300(3)(a), F.A.C., shall be exempt from the permitting requirements of this chapter, Chapters 62-212 and 62-4, F.A.C., if it meets all of the following criteria:

a. It would be subject to no unit-specific applicable requirement.

b. It would neither emit nor have the potential to emit:

(i) 500 pounds per year or more of lead and lead compounds expressed as lead;

(ii) 1,000 pounds per year or more of any hazardous air pollutant;

(iii) 2,500 pounds per year or more of total hazardous air pollutants; or

(iv) 5.0 tons per year or more of any other regulated pollutant.

c. Its emissions, in combination with the emissions of other units and activities at the facility, would not cause the facility to emit or have the potential to emit any pollutant in such amount as to make the facility a Title V source.

d. In the case of a proposed new emissions unit at an existing facility, the emissions of such unit, in combination with the emissions of any other proposed new or modified units and activities at the facility, would not result in a modification subject to the preconstruction review requirements of subparagraph 62-204.800(10)(d)2., Rule 62-212.400 or 62-212.500, F.A.C.

e. In the case of a proposed new pollutant-emitting activity, such activity would not constitute a modification of any existing non-exempt emissions unit at a non-Title V source or any existing non-insignificant emissions unit at a Title V source.

2. Generic Facility Exemption. A facility that is not entitled to a categorical exemption pursuant to paragraph 62-210.300(3)(a), F.A.C., shall be exempt from the permitting requirements of this chapter, Chapters 62-212 and 62-213, F.A.C., and Chapter 62-4, F.A.C., if all of the emissions units and activities within the facility, including any proposed new emissions units and activities, meet the exemption criteria of paragraph 62-210.300(3)(a), F.A.C., or subparagraph 62-210.300(3)(b)1., F.A.C., or if the facility meets all of the following criteria:

a. No emissions unit or pollutant-emitting activity within the facility would be subject to any unit-specific applicable requirement.

b. The facility would neither emit nor have the potential to emit:

(i) 1,000 pounds per year or more of lead and lead compounds expressed as lead;

(ii) 1.0 ton per year or more of any hazardous air pollutant;

(iii) 2.5 tons per year or more of total hazardous air pollutants;

(iv) 25 tons per year or more of carbon monoxide, nitrogen oxides and sulfur dioxide; or

(v) 10 tons per year or more of any other regulated pollutant.

c. The facility would neither emit nor have the potential to emit any pollutant in such amount as to make the facility a Title V source, nor would the facility be a Title V source for any other reason.

3. Temporary Exemption for Emissions Units at Certain Title V Sources. Except for an emissions unit that is subject to any applicable regulation or permitting requirement under Rule 62-212.400 or 62-212.500, F.A.C.; any emissions standard or other requirement adopted by reference prior to July 1, 1995, in Rule 62-204.800, F.A.C.; any requirement established pursuant to Rule 62-296.330, F.A.C.; or any Reasonably Available Control Technology (RACT) provisions under Rules 62-296.500 through 62-296.712, F.A.C.; an emissions unit that is described in a timely and complete permit application under Chapter 62-213, F.A.C., and not subject to an existing valid air permit, shall be exempt from the permitting requirements of this chapter, Chapter 62-4 and Rule 62-212.300, F.A.C., until a final determination on a permit application under Chapter 62-213, F.A.C., is made. In addition, no emissions unit shall be exempt under this paragraph if its emissions cause or contribute to a significant net emissions increase under Rule 62-212.400 or 62-212.500, F.A.C., which would trigger preconstruction review, or if it is constructed or modified, as defined under Rule 62-210.200, F.A.C., subsequent to November 23, 1994. Any applicant exercising this exemption shall provide notification of such exemption to the Department, and further authorizes the Department to inspect these emissions units at the Department’s discretion. Emissions units subject to existing valid permits shall continue to operate consistent with those permits as provided under subparagraph 62-213.420(1)(b)2., F.A.C. This exemption is available only to emissions units contained within either facilities that were Title V sources on or before October 25, 1995, and that commenced operation on or before that date, or facilities that became Title V sources by operation of law after October 25, 1995, and have timely applied for an initial Title V air operation permit.

4. Temporary Phosphogypsum Exemption. Until permitted pursuant to Chapter 62-213, F.A.C., phosphogypsum disposal areas are exempt from the requirement to obtain an air operation permit.

(c) Conditional Exemptions From Title V Air Permitting. The following facilities are exempt from the requirement to obtain a Title V air operation permit under the provisions of Chapter 62-213, F.A.C., but are not exempt from the requirement to obtain any other air permit as may be required under this rule unless also exempt from permitting under paragraph 62-210.300(3)(a) or (b), F.A.C., or Rule 62-4.040, F.A.C. A facility is not entitled to an exemption from Title V permitting under this rule if it is a Title V source pursuant to paragraph (f), (g), or (h) of the definition of “major source of air pollution” or the facility would be classified as a Title V source as a result of the combined potential to emit regulated pollutants of all emissions units at the facility.

1. Asphalt concrete plants, provided the following conditions are met:

a. The production rate of asphaltic concrete shall not exceed 500,000 tons in any consecutive twelve-month period.

b. Fuel oil consumption shall not exceed 1.2 million gallons in any consecutive twelve-month period.

c. Fuel oil shall not exceed 1.0 percent sulfur content, by weight. The owner shall maintain records to demonstrate that each shipment of fuel oil has 1.0 percent or less sulfur and that the sulfur content was determined by ASTM methods ASTM D4057-88 and ASTM D129-91, ASTM D2622-94 or ASTM D4294-90, adopted and incorporated by reference in subsection 62-297.440(1), F.A.C.

d. Particulate matter (PM) emissions shall not exceed 0.04 grains per dry standard cubic foot averaged over a three-hour period, if the facility is subject to 40 C.F.R. 60.90, Subpart I. If the facility is not subject to Subpart I, it shall not exceed the applicable particulate emission limiting standard pursuant to paragraph 62-296.320(4)(a), F.A.C., and its hours of operation shall not exceed 4,000 hours in any consecutive twelve-month period.

e. Fugitive PM emissions shall be controlled in accordance with the requirements of paragraph 62-296.320(4)(c), F.A.C.

f. Visible emissions (VE) shall not be equal to or greater than 20 percent opacity.

g. The owner or operator shall maintain records to document the monthly and the twelve-month rolling totals of tons of asphaltic concrete produced, the gallons of fuel oil consumed, and the hours of operation. Such records shall be retained for five years.

h. The owner or operator shall submit an Annual Operating Report for Air Pollutant Emitting Facility (DEP Form No. 62-210.900(5)) to the Department annually pursuant to subsection 62-210.370(3), F.A.C.

i. The owner or operator shall submit a stack test using EPA Reference Method 5 or 5A and a visible emission (VE) test using EPA Reference Method 9, incorporated and adopted by reference in Chapter 62-297, F.A.C., that demonstrate compliance with the applicable PM and VE standards, respectively, to the Department by March 15, 1996, and annually thereafter during each federal fiscal year (October 1-September 30). The initial tests shall have been conducted between March 16, 1995 and March 15, 1996.

j. The owner or operator of any asphalt plant in operation as of January 1, 1996, shall notify the appropriate permitting authority, with a copy to the Division of Air Resources Management, in writing, not later than March 15, 1996. Such notification shall include a statement that the facility is operating in compliance with the provisions of subparagraph 62-210.300(3)(c)1., F.A.C., and that the facility agrees to continue to operate in compliance with these provisions. If such facility has a valid air operation permit, the permit will be updated by the Department to incorporate the requirements of sub-subparagraphs 62-210.300(3)(c)1.a. through i., F.A.C. If such facility does not have a valid air operation permit, the facility shall apply to the Department for an air operation permit not later than March 15, 1996.

k. The owner or operator of any asphalt plant which commences operation after January 1, 1996, must request that the requirements of sub-subparagraphs 62-210.300(3)(c)1.a. through i., F.A.C., be incorporated into the facility’s air operation permit.

2. Bulk gasoline plants, provided the following conditions are met:

a. The facility operates no emissions units other than the bulk gasoline plant and emissions units which are exempt from permitting pursuant to the criteria of paragraph 62-210.300(3)(a) or (b), F.A.C., or have been exempted from permitting under Rule 62-4.040, F.A.C.;

b. The facility shall receive and distribute only petroleum-based lubricants, gasoline, diesel fuel, mineral spirits and kerosene.

c. The total storage capacity for gasoline at the facility shall not exceed 150,000 gallons.

d. The facility shall not exceed a throughput rate (receive and distribute) of 6.0 million gallons of gasoline in any consecutive twelve-month period.

e. The owner or operator of the facility maintains records to document the throughput rate of gasoline on a monthly basis. The owner or operator shall retain these records, available for Department inspection, for a period of at least five years.

f. The owner or operator submits a completed Bulk Gasoline Plant Air General Permit Notification Form (DEP Form No. 62-210.920(2)), showing entitlement to the use of the general permit, to the Department at least 30 days prior to beginning operations under the general permit.

g. The owner or operator of any bulk gasoline plant in operation as of January 1, 1996, which is not entitled to an air general permit shall notify the appropriate permitting authority, with a copy to the Division of Air Resources Management, in writing, not later than March 15, 1996. Such notification shall include a statement that the facility is operating in compliance with the provisions of subparagraph 62-210.300(3)(c)2., F.A.C., and that the facility agrees to continue to operate in compliance with these provisions. If such facility has a valid air operation permit, the permit will be updated by the Department to incorporate the requirements of sub-subparagraphs 62-210.300(3)(c)2.a. through c., F.A.C. If such facility does not have a valid air operation permit, the facility shall apply to the Department for an air operation permit not later than March 15, 1996. The owner or operator of any such bulk gasoline plant which commences operation after January 1, 1996, must request that the requirements of sub-subparagraphss 62-210.300(3)(c)2.a. through c., F.A.C., be incorporated into the facility’s air operation permit.

3. Facilities comprising heating units and general purpose internal combustion engines, provided the following conditions are met:

a. The facility operates no emissions units other than the heating units and general purpose internal combustion engines and emissions units which are exempt from permitting pursuant to the criteria of paragraph 62-210.300(3)(a) or (b), F.A.C., or have been exempted from permitting under Rule 62-4.040, F.A.C.

b. None of the heating units or general purpose internal combustion engines is subject to the Federal Acid Rain Program as defined at Rule 62-210.200, F.A.C.

c. Each of the heating units or general purpose internal combustion engines meets the general visible emissions standard of paragraph 62-296.320(4)(b), F.A.C.

d. Total fuel consumption by all heating units and general purpose internal combustion engines within the facility is limited to 250,000 gallons per year of diesel fuel, 22,000 gallons per year of gasoline, 35 million standard cubic feet per year of natural gas or propane, or an equivalent prorated amount if multiple fuels are used.

e. The owner or operator of the facility maintains records to document the fuel consumption, by type, for each emissions unit. The owner or operator shall retain these records, available for Department inspection, for a period of at least five years.

f. The owner or operator submits a completed Heating Units and General Purpose Internal Combustion Engines Air General Permit Notification Form (DEP Form No. 62-210.920(3)), showing entitlement to the use of the general permit, to the Department at least 30 days prior to beginning operations under the general permit.

4. Facilities comprising surface coating operations, provided the following conditions are met:

a. The facility operates no emissions units other than the surface coating operations and emissions units which are exempt from permitting pursuant to the criteria of paragraph 62-210.300(3)(a) or (b), F.A.C., or have been exempted from permitting under Rule 62-4.040, F.A.C.

b. Such operations are not subject to a volatile organic compound Reasonably Available Control Technology (RACT) emission limiting standard of Chapter 62-296, F.A.C.

c. The amount of coatings used shall include any solvents and thinners used in the process including those used for cleanup.

d. The total quantity of VOCs in such coatings is 44 pounds per day or less, averaged monthly.

e. The owner or operator of the facility maintains records to document the VOC content and the quantity of the coatings used. The owner or operator shall retain these records, available for Department inspection, for a period of at least five years.

f. The owner or operator submits a completed Surface Coating Operations Air General Permit Notification Form (DEP Form No. 62-210.920(4)), showing entitlement to the use of the general permit, to the Department at least 30 days prior to beginning operations under the general permit.

5. Facilities comprising polyester resin plastic products fabrication activities, provided the following conditions are met:

a. The facility operates no emissions units other than the polyester resin plastic products fabrication units and emissions units which are exempt from permitting pursuant to the criteria of paragraph 62-210.300(3)(a) or (b), F.A.C., or have been exempted from permitting under Rule 62-4.040, F.A.C.

b. Such operations are not subject to a volatile organic compound Reasonably Available Control Technology (RACT) emission limiting standard of Chapter 62-296, F.A.C.

c. The combined quantity of styrene-containing resin and gelcoat used shall not exceed 76,000 pounds (38 tons) in any consecutive twelve month period.

d. The owner or operator of the facility maintains records to document the quantity of resin and gelcoat used on a monthly basis. The owner or operator shall retain these records, available for Department inspection, for a period of at least five years.

e. The owner or operator submits a completed Polyester Resin Plastic Products Fabrication Air General Permit Notification Form (DEP Form No. 62-210.920(5)), showing entitlement to the use of the general permit, to the Department at least 30 days prior to beginning operations under the general permit.

6. Facilities comprising cast polymer operations, provided the following conditions are met:

a. The facility operates no emissions units other than the cast polymer operations and emissions units which are exempt from permitting pursuant to the criteria of paragraph 62-210.300(3)(a) or (b), F.A.C., or have been exempted from permitting under Rule 62-4.040, F.A.C.

b. Such operations are not subject to a volatile organic compound Reasonably Available Control Technology (RACT) emission limiting standard of Chapter 62-296, F.A.C.

c. The combined quantity of styrene-containing resin and gel coat used shall not exceed 284,000 pounds (142 tons) in any consecutive twelve-month period.

d. The owner or operator of the facility maintains records to document the quantity of resin and gel coat used on a monthly basis. The owner or operator shall retain these records, available for Department inspection, for a period of at least five years.

e. The owner or operator submits a completed Cast Polymer Operations Air General Permit Notification Form (DEP Form No. 62-210.920(6)), showing entitlement to the use of the general permit, to the Department at least 30 days prior to beginning operations under the general permit.

(4) Air General Permits.

(a) Title V Sources. Certain facilities are eligible to operate under the terms of an air general permit pursuant to the procedures and general conditions of Rule 62-213.300, F.A.C., Title V Air General Permits. These facilities are specified in Rule 62-213.300, F.A.C. Unless otherwise specified in Rule 62-213.300, F.A.C., the responsible official of any facility that is eligible and has submitted notification to use an air general permit pursuant to Rule 62-213.300, F.A.C., and who operates the facility in compliance with the terms and conditions of the air general permit shall not be required to obtain an air construction permit pursuant to subsection 62-210.300(1), F.A.C. In addition, such responsible official shall not be required to obtain a regular air operation permit pursuant to subsection 62-210.300(2), F.A.C., or a regular Title V air operation permit pursuant to Chapter 62-213, F.A.C.

(b) Facilities with Conditional Exemptions from Title V Air Permitting. No facility which contains an emissions unit, other than a unit described in an air general permit under this paragraph or a unit exempted from permitting pursuant to paragraph 62-210.300(3)(a) or (b), F.A.C., or Rule 62-4.040, F.A.C., shall be eligible to use any air general permit in this paragraph. No facility is eligible to use more than one air general permit under this paragraph. The following facilities are eligible to operate under the terms of an air general permit issued pursuant to the procedures and general conditions of paragraphs 62-210.300(4)(d) through (e), F.A.C., provided all existing air permits authorizing operation of the facility are surrendered, all requirements of this paragraph are met, and the facility complies with the terms and conditions of the particular air general permit throughout the term of the air general permit:

1. Bulk gasoline plants, provided the owner or operator timely submits a completed Bulk Gasoline Plant Air General Permit Notification Form (DEP Form No. 62-210.920(2)) to the Department and, throughout the term of the general permit:

a. The facility complies with the requirements for a conditional exemption from Title V permitting pursuant to subparagraph 62-210.300(3)(c)2., F.A.C.;

b. The facility is not subject to any Standard of Performance for New Stationary Sources (NSPS) requirement adopted by reference in subsection 62-204.800(7), F.A.C.; and

c. The facility is not subject to any volatile organic compound Reasonably Available Control Technology (RACT) requirement of Chapter 62-296, F.A.C.

2. Facilities comprising heating units and general purpose internal combustion engines, provided the owner or operator timely submits a completed Heating Units and General Purpose Internal Combustion Engines Air General Permit Notification Form (DEP Form No. 62-210.920(3)) to the Department and, throughout the term of the general permit:

a. The facility complies with the requirements for a conditional exemption from Title V permitting pursuant to subparagraph 62-210.300(3)(c)3., F.A.C.; and

b. The owner or operator voluntarily encourages pollution prevention through such measures as employing energy conservation measures to reduce the demand for heat from any heating units, maintaining heating units to ensure efficient heat recovery, considering the use of economizers to recycle waste heat back into the combustion air stream, developing operating procedures to reduce the load on any internal combustion engines, and considering the use of alternative fuels.

3. Facilities comprising surface coating operations, provided the owner or operator timely submits a completed Surface Coating Operations Air General Permit Notification Form (DEP Form No. 62-210.920(4)) to the Department and, throughout the term of the general permit:

a. The facility complies with the requirements for a conditional exemption from Title V permitting pursuant to subparagraph 62-210.300(3)(c)4., F.A.C.; and

b. The owner or operator voluntarily encourages pollution prevention through such measures as training employees involved in surface coating operations on methods of reducing VOC emissions by maintaining spray coating equipment to ensure effective application with a minimum of overspray, monitoring the coating thickness to avoid excessive coating, considering the use of low-VOC coatings (e.g., waterborne, ultraviolet cured, or powder coatings), implementing inventory control practices to prevent spillage, and implementing management practices to reduce VOC emissions during cleanup (e.g., spraying light colored coatings before dark colored coatings to reduce the number of cleaning cycles, recycling cleaning solvents or using water-based cleaners).

4. Facilities comprising polyester resin plastic products fabrication activities, provided the owner or operator timely submits a completed Polyester Resin Plastic Products Fabrication Air General Permit Notification Form (DEP Form No. 62-210.920(5)) to the Department and, throughout the term of the general permit:

a. The facility complies with the requirements for a conditional exemption from Title V permitting pursuant to subparagraph 62-210.300(3)(c)5., F.A.C.;

b. The facility complies with the objectionable odor prohibition of subsection 62-296.320(2), F.A.C.; and

c. The owner or operator voluntarily encourages pollution prevention through such measures as training employees involved in product fabrication on methods of reducing evaporative losses by lessening the exposure of fresh resin surfaces to the air, maintaining spray lay-up equipment to ensure effective application with a minimum of overspray, monitoring the coating thickness of avoid excessive resin/gelcoat application, implementing inventory control practices to prevent spillage, and managing cleanup solvents.

5. Facilities comprising cast polymer operations, provided the owner or operator timely submits a completed Cast Polymer Operations Air General Permit Notification Form (DEP Form No. 62-210.920(6)) to the Department and, throughout the term of the general permit:

a. The facility complies with the requirements for a conditional exemption from Title V permitting pursuant to subparagraph 62-210.300(3)(c)6., F.A.C.;

b. The facility complies with the objectionable odor prohibition of subsection 62-296.320(2), F.A.C.; and

c. The owner or operator voluntarily encourages pollution prevention through such measures as training employees involved in product fabrication on methods of reducing evaporative losses by lessening the exposure of fresh resin surfaces to the air, maintaining spray lay-up equipment to ensure effective application with a minimum of overspray, monitoring the coating thickness to avoid excessive resin/gel coat application, implementing inventory control practices to prevent spillage, and managing cleanup solvents.

(c) Other Non-Title V Air General Permits. No facility which contains an emissions unit, other than a unit described in an air general permit under this paragraph or a unit exempted from permitting pursuant to paragraph 62-210.300(3)(a) or (b), F.A.C., or Rule 62-4.040, F.A.C., shall be eligible to use any air general permit in this paragraph. Unless specifically authorized by the particular air general permit, no facility is eligible to use more than one air general permit under this paragraph. In no event, however, shall any emissions unit be eligible to use any air general permit in this paragraph if the unit would be a Title V source as defined at Rule 62-210.200, F.A.C., be located at or relocated to a Title V source, or create a Title V source with other facilities or emissions units. The following facilities are eligible to operate under the terms of an air general permit pursuant to the procedures and general conditions of paragraphs 62-210.300(4)(d) through (e), F.A.C., provided all existing air permits authorizing operation of the facility are surrendered, all requirements of this paragraph are met, and the facility complies with the terms and conditions of the particular air general permit throughout the term of the air general permit:

1. Volume reduction, mercury recovery, and mercury reclamation processes as defined in and subject to the requirements of Rule 62-296.417, F.A.C., provided the owner or operator submits a completed Volume Reduction, Mercury Recovery or Mercury Reclamation Air General Permit Notification Form (DEP Form No. 62-210.920(1)) to the Department at least 30 days prior to beginning operations under the general permit and, throughout the term of the general permit, the facility does not emit or have the potential to emit 10 tons per year or more of mercury.

2. Concrete batching plants as subject to the requirements of Rule 62-296.414, F.A.C., provided:

a. The owner or operator timely submits a completed Concrete Batching Plant Air General Permit Notification Form (DEP Form No. 62-210.920(7)) to the Department. The owner or operator of any proposed new concrete batching plant shall publish a notice of intent to use the general permit in a newspaper of general circulation in the area affected by the proposed project no more than 21 days prior to submitting a completed notification form to the Department, shall submit a completed notification form with proof of notice publication to the Department at least 30 days prior to beginning construction, and shall demonstrate compliance no more than 30 days after beginning operation. The Department shall provide the format for the notice of intent;

b. Throughout the term of the air general permit, the owner or operator complies with the requirements of Rule 62-296.414, F.A.C.;

c. The owner or operator of any relocatable concrete batching plant proposing to change location shall submit a Facility Relocation Notification Form (DEP Form No. 62-210.900(6)) to the Department at least 30 days prior to relocation;

d. The owner or operator of a stationary concrete batching plant using an air general permit may operate a stationary nonmetallic mineral processing plant using an air general permit at the same location provided all concrete batching plant units operate under a single concrete batching plant air general permit, all nonmetallic mineral processing plant units operate under a single nonmetallic mineral processing plant air general permit, and the resultant facility contains no additional nonexempt units and would not be a Title V source;

e. The owner or operator of a stationary concrete batching plant using an air general permit may operate, or allow the operation of, one or more relocatable nonmetallic mineral processing plants using individual air general permits at the same location as the concrete batching plant provided the resultant facility contains no additional nonexempt units, the total combined annual facility-wide fuel oil usage of all plants is less than 240,000 gallons per calendar year, the material processed is less than 10 million tons per calendar year, and the fuel oil sulfur content does not exceed 0.5%, by weight. The owner or operator of the concrete batching plant shall maintain a log book to account for fuel consumption and material processed on a monthly basis. Fuel supplier certifications shall be maintained to account for the sulfur content of the fuel being burned; and

f. The owner or operator of multiple relocatable concrete batching plants using individual concrete batching plant air general permits may operate more than one such plant at the same location provided the resultant facility contains no additional nonexempt units and would not be a Title V source.

3. Human crematories as subject to the requirements of subsection 62-296.401(5), F.A.C., provided:

a. The owner or operator obtains an air construction permit pursuant to subsection 62-210.300(1), F.A.C., and at least 30 days prior to the expiration date of any air construction or existing air operation permit the owner or operator submits a completed Human Crematory Air General Permit Notification Form (DEP Form No. 62-210.920(8)) to the Department;

b. Throughout the term of the air general permit, the owner or operator complies with the requirements of subsection 62-296.401(5), F.A.C.; and

c. The owner or operator may use a human crematory air general permit and an animal crematory air general permit at the same facility provided all human crematory units operate under a single human crematory air general permit and all animal crematory units operate under a single animal crematory air general permit.

4. Animal crematories with aggregate facility design capacity to cremate 500 pounds per hour or less, as subject to the requirements of subsection 62-296.401(6), F.A.C., provided:

a. The owner or operator obtains an air construction permit pursuant to subsection 62-210.300(1), F.A.C., and at least 30 days prior to the expiration date of any air construction or existing air operation permit the owner or operator submits a completed Animal Crematory Air General Permit Notification Form (DEP Form No. 62-210.920(9)) to the Department;

b. Throughout the term of the air general permit, the owner or operator complies with the requirements of subsection 62-296.401(6), F.A.C.; and

c. The owner or operator may use a human crematory air general permit and an animal crematory air general permit at the same facility provided all human crematory units operate under a single human crematory air general permit and all animal crematory units operate under a single animal crematory air general permit.

5. Nonmetallic mineral processing plants, provided the owner or operator timely submits a completed Nonmetallic Mineral Processing Plant Air General Permit Notification Form (DEP Form No. 62-210.920(10)) to the Department, and, throughout the term of the general permit complies with the following terms and conditions:

a. For purposes of this rule, the definitions of 40 CFR 60.671, adopted and incorporated by reference at Rule 62-204.800, F.A.C., shall apply;

b. The owner or operator of any relocatable nonmetallic mineral processing plant proposing to change location shall notify the Department by phone prior to changing location and submit a Facility Relocation Notification Form (DEP Form No. 62-210.900(6)) to the Department no later than one (1) business day following relocation;

c. For all relocatable nonmetallic mineral processing plants, except those located at mines or quarries and processing only material from onsite natural deposits, and for all stationary nonmetallic mineral processing plants processing dry material, the owner or operator shall have a water suppression system with spray bars located at the feeder(s), the entrance and exit of the crusher(s), the classifier screens, and the conveyor drop points;

d. The owner or operator shall comply with paragraph 62-296.320(4)(c), F.A.C., using the following reasonable precautions:

(i) Unconfined emissions that might be generated from various activities throughout a nonmetallic mineral processing plant processing dry material shall be controlled by using a water suppression system with spray bars located at the feeder(s), the entrance and exit of the crusher(s), the classifier screens, and the conveyor drop points.

(ii) Unconfined emissions that might be generated by vehicular traffic or wind shall be controlled by applying water (by water trucks equipped with spray bars) or effective dust suppressant(s) on a regular basis to all stockpiles, roadways and work-yards where this nonmetallic mineral processing plant is located;

e. The owner or operator shall comply with the following emissions standards, as applicable:

(i) Stack emissions from any crusher, grinding mill, screening operation, bucket elevator, transfer point on belt conveyors, bagging operation, storage bin, enclosed truck or railcar loading station, or any other affected emission point subject to 40 CFR Part 60, Subpart OOO, adopted and incorporated by reference at Rule 62-204.800, F.A.C., shall not contain particulate matter in excess of 0.05 grams per dry standard cubic meter (g/dscm) nor exceed 7% opacity, unless the stack emissions are discharged from a wet scrubbing control device.

(ii) Stack emissions from any baghouse that controls emissions from only an individual, enclosed storage bin subject to 40 CFR Part 60, Subpart OOO, adopted and incorporated by reference at Rule 62-204.800, F.A.C., shall not exceed 7% opacity.

(iii) Visible emissions from any grinding mill, screening operation, bucket elevator, transfer point on belt conveyors, bagging operation, storage bin, enclosed truck or railcar loading station, or any other affected emission point subject to 40 CFR Part 60, Subpart OOO, adopted and incorporated by reference at Rule 62-204.800, F.A.C., shall not exceed 10% opacity; and visible emissions from any crusher without a capture system subject to 40 CFR Part 60, Subpart OOO, shall not exceed 15% opacity.

(iv) If any crusher, grinding mill, screening operation, bucket elevator, transfer point on belt conveyors, bagging operation, storage bin, enclosed truck or railcar loading station, or any other emission point subject to 40 CFR Part 60, Subpart OOO, adopted and incorporated by reference at Rule 62-204.800, F.A.C., is enclosed in a building, then each enclosed emission point must comply with the emission limits in sub-subparagraphs 62-210.300(4)(c)5.e.(i) through (iii), F.A.C., or the building enclosing the emission point(s) shall not discharge any visible fugitive emissions, except emissions from a vent, and the vent emissions shall not exceed the stack emissions limits of sub-sub-subparagraph 62-210.300(4)(c)5.e.(i), F.A.C.

(v) Visible emissions from any crusher, grinding mill, screening operation, bucket elevator, transfer point on belt conveyors, bagging operation, storage bin, enclosed truck or railcar loading station, or any other emission point not subject to 40 CFR Part 60, Subpart OOO, adopted and incorporated by reference at Rule 62-204.800, F.A.C., shall be less than 20% opacity, pursuant to subparagraph 62-296.320(4)(b)1., F.A.C.

(vi) Truck dumping of nonmetallic minerals into any screening operation, feed hopper, or crusher subject to 40 CFR Part 60, Subpart OOO, adopted and incorporated by reference at Rule 62-204.800, F.A.C., is exempt from the emissions standards of sub-subparagraph 62-210.300(4)(c)5.e., F.A.C.;

f. The owner or operator shall ensure that wet screening operations and subsequent screening operations, bucket elevators, and belt conveyors that process saturated material in the production line up to the next crusher, grinding mill or storage bin and are subject to 40 CFR Part 60, Subpart OOO, adopted and incorporated by reference at Rule 62-204.800, F.A.C., do not discharge any visible emissions. The owner or operator shall also ensure that screening operations, bucket elevators, and belt conveyors in the production line downstream of wet mining operations, where such screening operations, bucket elevators, and belt conveyors process saturated materials up to the first crusher, grinding mill, or storage bin in the production line and are subject to 40 CFR Part 60, Subpart OOO, adopted and incorporated by reference at Rule 62-204.800, F.A.C., do not discharge any visible emissions;

g. The owner or operator of a nonmetallic mineral processing plant subject to 40 CFR Part 60, Subpart OOO, adopted and incorporated by reference at Rule 62-204.800, F.A.C., and using a wet scrubber to control emissions shall comply with the monitoring requirements of 40 CFR 60.674, adopted and incorporated by reference at Rule 62-204.800, F.A.C.;

h. The owner or operator shall provide a compliance demonstration with the emission standards of sub-subparagraph 62-210.300(4)(c)5.e., F.A.C., along with a request for renewal of authorization for use of the air general permit. The owner or operator of any new facility shall demonstrate initial compliance with the emission standards of sub-subparagraph 62-210.300(4)(c)5.e., F.A.C., prior to beginning commercial operation and shall demonstrate renewal compliance with the emission standards of sub-subparagraph 62-210.300(4)(c)5.e., F.A.C., within 60 days prior to the anniversary of the initial air general permit notification form submittal date. The owner or operator of any existing facility shall demonstrate compliance with the emission standards of sub-subparagraph 62-210.300(4)(c)5.e., F.A.C., within 60 days prior to submitting an air general permit notification form and shall demonstrate renewal compliance within 60 days prior to the anniversary of the initial air general permit notification form submittal date. For purposes of the testing requirements of this rule, the visible emission reference test method shall be EPA Method 9, the visible fugitive emission reference test method shall be EPA Method 22, the particulate matter reference test method shall be either EPA Method 5 or 17, and the test procedures shall meet all applicable requirements of Chapter 62-297, F.A.C., 40 CFR 60.675, and 40 CFR Part 60, Appendix A, adopted and incorporated by reference at Rule 62-204.800, F.A.C.;

i. The owner or operator shall meet all applicable reporting and recordkeeping requirements of Chapter 62-297, F.A.C. and 40 CFR 60.676, adopted and incorporated by reference at Rule 62-204.800, F.A.C.;

j. The owner or operator of a stationary nonmetallic mineral processing plant using an air general permit may operate a stationary concrete batching plant using an air general permit at the same location provided all nonmetallic mineral processing plant units operate under a single nonmetallic mineral processing plant air general permit, all concrete batching plant units operate under a single concrete batching plant air general permit, and the resultant facility contains no additional nonexempt units and would not be a Title V source;

k. The owner or operator of a stationary nonmetallic mineral processing plant using an air general permit may operate, or allow the operation of, one or more relocatable concrete batching plants using individual air general permits at the same location as the nonmetallic mineral processing plant provided the resultant facility contains no additional nonexempt units and would not be a Title V source;

l. The owner or operator of multiple relocatable nonmetallic mineral processing plants using individual nonmetallic mineral processing plant air general permits may operate more than one such plant at the same location provided the resultant facility contains no additional nonexempt units, the total combined annual facility-wide fuel oil usage of all plants is less than 240,000 gallons per calendar year, the material processed is less than 10 million tons per calendar year, and the fuel oil sulfur content does not exceed 0.5%, by weight. The owner or operator of the nonmetallic mineral processing plants shall maintain a log book to account for fuel consumption and material processed on a monthly basis. Fuel supplier certifications shall be maintained to account for the sulfur content of the fuel being burned; and

m. If a relocatable nonmetallic mineral processing plant is used to perform a routine function of a facility subject to regular air permitting, such as crushing recycled asphalt (rap) at an asphalt plant, it shall not operate under the authority of an air general permit. In such case, the regularly permitted facility air construction or air operation permit(s) must provide for operation of the nonmetallic mineral processing plant as an emission unit. If a relocatable nonmetallic mineral processing plant is used at a regularly permitted facility for a non-routine activity, such as destruction of a building, it may do so under the authority of its air general permit. In either case, the resultant facility shall not be a Title V source.

(d) General Procedures.

1. Eligibility Determination. The owner or operator of the facility or emissions unit shall determine its eligibility for an air general permit pursuant to the applicability criteria of paragraph 62-210.300(4)(b) or (c), F.A.C.

a. Unless otherwise specified in paragraph 62-210.300(4)(b) or (c), F.A.C., the owner or operator of any facility or emissions unit that is eligible and has submitted notification to use an air general permit pursuant to paragraph 62-210.300(4)(b) or (c), F.A.C., and who operates the facility or emissions unit in compliance with the terms and conditions of the air general permit shall not be required to obtain an air construction permit pursuant to subsection 62-210.300(1), F.A.C. In addition, such owner or operator shall not be required to obtain a regular air operation permit pursuant to subsection 62-210.300(2), F.A.C.

b. If a facility or emissions unit permitted by an air general permit under this rule at any time becomes ineligible for the use of the air general permit, or if any facility or emissions unit utilizing an air general permit is determined to have been initially ineligible for use of the air general permit, it shall be subject to enforcement action for constructing or operating without an air permit under subsection 62-210.300(1) or (2), F.A.C.

c. For each facility or emissions unit intending to operate under the provisions of an air general permit, the owner or operator must complete and submit the correct notification form for the specific general permit to be utilized, as set forth in paragraph 62-210.300(4)(b) through (c), F.A.C., to give notice to the Department of intent to use one of the air general permits listed in this rule.

2. Processing Fee. The notification must be accompanied by the appropriate general permit processing fee pursuant to Rule 62-4.050, F.A.C.

3. Administrative Corrections. Within 30 days of any changes requiring corrections to information contained in the notification form, the owner or operator shall notify the Department in writing. Such changes shall include:

a. Any change in the name of the authorized representative or facility address or phone number; or

b. Any other similar minor administrative change at the facility or emissions unit.

4. Equipment Changes. In case of the installation of new process equipment, alteration of existing process equipment without replacement, or the replacement of existing process equipment with equipment substantially different than that noted on the most recent notification form, the owner or operator shall submit a new and complete general permit notification form with the appropriate fee pursuant to Rule 62-4.050, F.A.C., to the Department.

5. Violation of Permit. The air general permit is valid only for the specific activity indicated. Any deviation from the specified activity and the conditions for undertaking that activity is a violation of the permit. The owner or operator is placed on notice that violation of the permit constitutes grounds for revocation and suspension pursuant to Rule 62-4.100 and subsection 62-4.530(4), F.A.C., and initiation of enforcement action pursuant to Sections 403.141 through 403.161, F.S. No revocation shall become effective except after notice is served by personal service, certified mail, or newspaper notice pursuant to Section 120.60(5), F.S., upon the person or persons named therein and a hearing held, if requested within the time specified in the notice. The notice shall specify the provision of the law or rule alleged to be violated, or the permit condition or Department order alleged to be violated, and the facts alleged to constitute a violation thereof.

6. Nullification of Eligibility. Eligibility for use of an air general permit under subsection 62-210.300(4), F.A.C. is nullified by submission of false or inaccurate information in the notification form for use of the air general permit or in the required reports.

7. Use of Permit. Any facility or emissions unit eligible to operate under the terms of an air general permit may use the permit 30 days after giving notice to the Department without any agency action.

(e) General Conditions. All terms, conditions, requirements, limitations, and restrictions set forth in this rule are “general permit conditions” and are binding upon the owner or operator of any facility or emissions unit utilizing an air general permit pursuant to this rule.

1. A permittee’s use of a general permit is limited to five years. No later than 30 days prior to the fifth anniversary of the filing of intent to use the general permit, the owner or operator shall submit a new notice of intent which shall contain all current information regarding the facility or emissions unit. Eligibility to use the general permit is not transferable and does not follow a change in ownership of the facility or emissions unit. Prior to any sale, other change of ownership, or permanent shutdown of the facility, the owner or operator is encouraged to notify the Department of the pending action. The owner shall remain liable for corrective actions that may be required as a result of any violations occurring in the time after the sale or legal transfer of the facility or emissions unit, but before a new owner is entitled to use an air general permit.

2. The general permit is valid only for the specific activity indicated. Any deviation from the specified activity and the conditions for undertaking that activity shall constitute a violation of the permit.

3. The general permit does not convey any vested rights or any exclusive privileges, nor does it authorize any injury to public or private property nor any invasion of personal rights. It does not authorize any infringement of federal, state, or local laws or regulations.

4. The general permit does not relieve the owner or operator of the facility or emissions unit from liability and penalties when the construction or operation of the permitted activity causes harm or injury to human health or welfare; causes harm or injury to animal, plant or aquatic life; or causes harm or injury to property. It does not allow the owner or operator to cause pollution in contravention of Florida law.

5. The general permit conveys no title to land or water, nor does it constitute state recognition or acknowledgment of title.

6. The owner or operator shall make every reasonable effort to conduct the specific activity authorized by the general permit in a manner that will minimize any adverse effects on adjacent property or on public use of the adjacent property, where applicable, and on the environment, including fish, wildlife, natural resources, water quality, or air quality.

7. The owner or operator shall allow a duly authorized representative of the Department access to the permitted facility, emissions unit, or activity at reasonable times to inspect and test, upon presentation of credentials or other documents as may be required by law, to determine compliance with the general permit and Department rules.

8. The owner or operator shall maintain any permitted facility, emissions unit, or activity in good condition. Throughout the term of the air general permit, the owner or operator shall ensure that the facility or emissions unit maintains its eligibility to use the air general permit and complies with all terms and conditions of the air general permit.

9. The air general permit shall be effective until suspended, revoked, surrendered, expired, or nullified pursuant to this rule. The general permit may be modified, suspended or revoked in accordance with Chapter 120, Florida Statutes, if the Secretary determines that there has been a violation of any of the terms or conditions of the permit, there has been a violation of state water quality standards or state air quality standards, or the permittee has submitted false, incomplete or inaccurate data or information.

10. The air general permit does not authorize any demolition or renovation of the facility or emissions unit or its parts or components which involves asbestos removal. The air general permit does not constitute a waiver of any of the requirements of Chapter 62-257, F.A.C., and 40 CFR Part 61, Subpart M, National Emission Standard for Asbestos, adopted and incorporated by reference in Rule 62-204.800, F.A.C.

11. The general permit does not authorize any open burning.

12. No person shall circumvent any air pollution control device or allow the emission of air pollutants without the proper operation of all applicable air pollution control devices.

13. If, for any reason, the owner or operator of any facility or emissions unit operating under an air general permit pursuant to paragraph 62-210.300(4)(a), F.A.C., does not comply with or will be unable to comply with any condition or limitation of the permit, the permittee shall immediately provide the Department with the following information:

a. A description of and cause of noncompliance; and

b. The period of noncompliance, including dates and times; or, if not corrected, the anticipated time the noncompliance is expected to continue, and steps being taken to reduce, eliminate, and prevent recurrence of the noncompliance. The permittee shall be responsible for any and all damages which may result.

14. The general permit does not eliminate the necessity for obtaining any other federal, state or local permits that may be required, or allow the permittee to violate any more stringent standards established by federal or local law.

15. Each facility located within the borders of any of the following counties shall also comply with the requirements of that county:

a. Broward County.

b. Dade County.

c. Duval County.

d. Hillsborough County.

e. Orange County.

f. Palm Beach County.

g. Pinellas County.

h. Sarasota County.

(5) Notification of Startup. The owners or operator of any emissions unit or facility which has a valid air operation permit which has been shut down more than one year, shall notify the Department in writing of the intent to start up such emissions unit or facility, a minimum of 60 days prior to the intended startup date.

(a) The notification shall include information as to the startup date, anticipated emission rates or pollutants released, changes to processes or control devices which will result in changes to emission rates, and any other conditions which may differ from the valid outstanding operation permit.

(b) If, due to an emergency, a startup date is not known 60 days prior thereto, the owner shall notify the Department as soon as possible after the date of such startup is ascertained.

(6) Emissions Unit Reclassification.

(a) Any emissions unit whose operation permit has been revoked as provided for in Chapter 62-4, F.A.C., shall be deemed permanently shut down for purposes of Rule 62-212.500, F.A.C. Any emissions unit whose permit to operate has expired without timely renewal or transfer may be deemed permanently shut down, provided, however, that no such emissions unit shall be deemed permanently shut down if, within 20 days after receipt of written notice from the Department, the emissions unit owner or operator demonstrates that the permit expiration resulted from inadvertent failure to comply with the requirements of Rule 62-4.090, F.A.C., and that the owner or operator intends to continue the emissions unit in operation, and either submits an application for an air operation permit or complies with permit transfer requirements, if applicable.

(b) If the owner or operator of an emissions unit which is so permanently shut down, applies to the Department for a permit to reactivate or operate such emissions unit, the emissions unit will be reviewed and permitted as a new emissions unit.

(7) Transfer of Air Permits.

(a) An air permit is transferable only after submission of an Application for Transfer of Air Permit (DEP Form 62-210.900(7))and Department approval in accordance with Rule 62-4.120, F.A.C. For Title V permit transfers only, a complete application for transfer of air permit shall include the requirements of 40 CFR 70.7(d)(1)(iv), adopted and incorporated by reference at Rule 62-204.800, F.A.C. Within 30 days after approval of the transfer of permit, the Department shall update the permit by an administrative permit correction pursuant to Rule 62-210.360, F.A.C.

(b) For an air general permit, the provisions of paragraph 62-210.300(7)(a) and Rule 62-4.120, F.A.C., do not apply. Thirty (30) days before using an air general permit, the new owner must submit an air general permit notification to the Department in accordance with subsection 62-210.300(4) or paragraph 62-213.300(2)(b), F.A.C.

Specific Authority 403.061 FS. Law Implemented 403.031, 403.061, 403.087, 403.814 FS. History–Formerly 17-2.210, Amended 11-28-93, Formerly 17-210.300, Amended 11-23-94, 4-2-95, 4-18-95, 10-16-95, 1-2-96, 3-13-96, 3-21-96, 5-13-96, 8-15-96, 10-7-96, 5-20-97, 11-13-97, 2-5-98, 2-11-99, 4-16-01, 6-21-01, 7-6-05, 2-2-06.