62-296.409 Sulfur Recovery Plants.

These limits are applicable to plants recovering sulfur from crude oil gas.

(1) New Plants – 0.004 pounds of sulfur dioxide per pound of sulfur input to the recovery system or 0.004 pounds of sulfur dioxide per pound of sulfur removed from an oil well.

(2) Existing Plants (for which a valid Department Construction permit was issued prior to July 1, 1973) – 0.08 pounds of sulfur dioxide per pound of sulfur input to the recovery system or 0.08 pounds of sulfur dioxide per pound of sulfur removed from crude oil or gas processed.

(3) Test Methods and Procedures. All emissions tests performed pursuant to the requirements of this rule shall comply with the following requirements.

(a) The test method for sulfur dioxide shall be EPA Method 6, incorporated and adopted by reference in Chapter 62-297, F.A.C. The minimum sample volume shall be 0.71 dry standard cubic feet. Two 20 minute samples (±5 minutes) per run required.

(b) Test procedures shall meet all applicable requirements of Chapter 62-297, F.A.C.

Specific Authority 403.061 FS. Law Implemented 403.021, 403.031, 403.061, 403.087 FS. History–Formerly 17-2.600(9), 17-296.409, Amended 11-23-94, 1-1-96.