62N-16.035 Transfers.

(1) Pollutant transfers which are not subject to the requirements contained in 33 C.F.R., Part 154 or Chapters 62-761 or 62-762, Florida Administrative Code, shall meet the following minimum requirements:

(a) All equipment used for transferring pollutants shall be kept and maintained in good repair and excellent operating condition.

(b) Hoses used for a transfer of pollutants shall be in good condition with no cracks or bubbles in their outer cover material. Hoses shall be maintained so that the inner lining or core is not exposed to damage from external forces. Hose and nozzle connections must be in good condition and not leaking. The fittings, clamps, and bands must be compatible to the pollutant being transferred and must be in good condition and securely attached to the hose. These fittings, clamps, and bands shall be used only for the purpose for which they are designed.

(c) All systems will be equipped with hard connections or delivery nozzles and the nozzles shall hang vertically while not in use and will not be lying on the ground or dock. The transfer equipment shall be equipped with an emergency shutdown device unless gravity fed. The person in charge, or his designee, must be in the proximity and have immediate access to the emergency shut-down device during all transfers.

(d) Any pollutant remaining in a hose after a transfer shall not be drained onto the ground or into the water.

(e) Dispensers located in such a manner that they are subject to being damaged or destroyed by impact shall be equipped with safety impact valves. These safety impact valves shall stop the flow of pollutants if the dispensers are damaged or destroyed by impact.

(2) The provisions of this section shall be effective by July 1, 1993.

Specific Authority 376.07 FS. Law Implemented 376.041 FS. History–New 3-2-93, Formerly 16N-16.035, Amended 10-17-94.