Notice of Bid/Request for Proposal

DEPARTMENT OF MILITARY AFFAIRS

220009 CBJTC 4600 Area Avenues Paving

STATE OF FLORIDA, DEPARTMENT OF MILITARY AFFAIRS

PUBLIC ANNOUNCEMENT

INVITATION TO BID

Issuing Agency: Department of Military Affairs

Project Number and Name: 220009 – CBJTC 4600 Area Avenues Paving (Plant City, Pinellas Park, and Quincy Avenues)

Project Location: Camp Blanding Joint Training Center (CBJTC), Starke, FL 32091

Statement of Work: Repave Plant City, Pinellas Park, and Quincy Avenues in the 4600 block between Miami Street and Sandford Street at Camp Blanding Joint Training Center.  There will be no milling of the road.  Sweep and tack road surface prior to installing a levelling course.  Final paving to consist of 1 ½” of 12.5 mix per FDOT Standards.  There shall be a 2% fall from the centerline of the road to each edge of road. Roads are 22’ wide with an approximate total area of road surface of 14,960 sq. yds.

Prior to paving, clean/regrade ditches/swales on both sides of the avenues with a 3:1 slope with a maximum depth of 18”, approximately 12,240 linear feet, and replace/add approximately 192 linear feet of corrugated culverts.  Provide for approximately 73,440 sq. ft. of hydro-seeding for all new ditch areas.

Contractor to remove and dispose of all construction and debris off of CBJTC property.  All new paving to be swept upon completion of project.

Estimated Construction Cost (range): $275,000 - $300,000

Type of Contractor: Licensed Contractor

Date of VBS Posting: August 17, 2021

Non-Mandatory Site Visit Date: As stated on the Vendor Bid System

Bid Opening Date: As stated on the Vendor Bid System (late bids will not be accepted)

Point of Contact: Dept. of Military Affairs, CFMO Contract Management (904)823-0256 or e-mail: ng.fl.flarng.list.cfmo-contracting@mail.mil

FOR COMPLETE INFORMATION AND SUBMISSION REQUIREMENTS PLEASE REFER TO THE MYFLORIDA.COM VENDOR BID SYSTEM AT: http://vbs.dms.state.fl.us/vbs/main_menu.