## 64E-5.330 Discharge by Release into Sanitary Sewerage.

(1) A licensee can discharge licensed material into sanitary sewerage if each of the following conditions is satisfied:

(a) The material is readily soluble or is readily dispersible biological material in water;

(b) The quantity of licensed radioactive material that the licensee releases into the sewer in 1 month divided by the average monthly volume of water released into the sewer by the licensee does not exceed the concentration listed in State of Florida Bureau of Radiation Control ALIs, DACs, and Effluent Concentrations, July 1993, Table III;

(c) If more than one radionuclide is released, the following conditions must also be satisfied;

1. The licensee shall determine the fraction of the limit in State of Florida Bureau of Radiation Control ALIs, DACs, and Effluent Concentrations, July 1993, Table III represented by discharges into sanitary sewerage by dividing the actual monthly average concentration of each radionuclide released by the licensee into the sewer by the concentration of that radionuclide listed in State of Florida Bureau of Radiation Control ALIs, DACs, and Effluent Concentrations, July 1993, Table III; and

2. The sum of the fractions for each radionuclide required by subparagraph 64E-5.330(1)(c)1., F.A.C., does not exceed unity; and

(d) The total quantity of licensed radioactive material that the licensee releases into the sanitary sewerage in a year does not exceed 5 curies (185 gigabecquerels) of hydrogen 3, 1 curie (37 gigabecquerels) of carbon 14, and 1 curie (37 gigabecquerels) of all other radioactive materials combined.

(2) Excreta from individuals undergoing medical diagnosis or therapy with radioactive material are not subject to the limitations contained in subsection 64E-5.330(1), F.A.C.

Rulemaking Authority 404.051, 404.081 FS. Law Implemented 404.022, 404.051(1), (4), 404.081 FS. History–New 1-1-94, Formerly 10D-91.463.