## 64E-11.007 Sanitary Facilities and Controls.

(1) Water supply – The water supply shall be adequate, of safe sanitary quality and from an approved source in accordance with provisions of Chapters 62-550 and 62-555, or 64E-8, F.A.C. Hot and cold running water under pressure shall be provided in all areas where food is prepared and where equipment and multi-use utensils are washed.

(a) Transportation of water – All potable water not provided directly by pipe to the food service establishment from the source shall be transported in a bulk water transport system and shall be delivered to a closed water system.

(b) Bottled water – Bottled and packaged potable water shall be obtained from a source that complies with the requirements of Sections 500.147(3) and (4), F.S., and shall be handled and stored in a way that protects it from contamination. Bottled and packaged potable water shall be dispensed from the original container.

(c) Steam – Steam used in contact with food or food-contact surfaces shall be free from any materials or additives other than those specified in Title 21, Code of Federal Regulations 173.310.

(d) Ice – Ice making machines shall utilize water from an approved source and shall be constructed, located, installed, operated and maintained so as to prevent contamination of the ice. They shall be kept clean and shall be stored and handled in a sanitary manner.

(2) Sewage disposal – Sewage shall be disposed of in a public sewerage system or other approved sewerage system in accordance with provisions of Chapter 64E-6 or 62-600, F.A.C., whichever is applicable. Grease interceptors shall be readily accessible for cleaning. Grease interceptors shall be designed and installed in accordance with provisions of Chapter 64E-6, F.A.C., or the applicable plumbing authority.

(3) Plumbing – Plumbing shall be sized, installed and maintained in accordance with provisions of the applicable plumbing authority. The plumbing shall provide adequate quantities of potable water to required locations throughout the establishment, prevent contamination of the water supply, properly convey sewage and liquid wastes from the establishment to the sewerage system; and shall not constitute a source of contamination of food, equipment or utensils or create an unsanitary condition or nuisance.

(a) Backflow – The potable water system shall be installed to preclude the possibility of backflow. Devices shall be installed and maintained to protect against backflow and back siphonage at all fixtures and equipment where an air gap at least twice the diameter of the water supply inlet is not provided between the water supply inlet and the fixture’s flood level rim. A hose shall not be attached to a faucet unless a backflow prevention device is installed. Any faucet equipped with a hose fitting shall be protected by a backflow protection device.

(b) Drains – There shall be no direct connection between the sewerage system and any drains originating from equipment in which food, portable equipment or utensils are placed. When a dishwashing machine is located within 5 feet of a trapped floor drain, the dishwasher waste outlet may be connected directly to the inlet side of a properly vented floor drain trap.

(4) Toilet facilities – Each food service establishment shall be provided with adequate and conveniently located toilet facilities for its employees and patrons in accordance with provisions of the applicable plumbing authority or, where no plumbing code has been adopted locally, with Chapter 64E-10, F.A.C. Food service establishments constructed or extensively remodeled after the effective date of these rules are required to comply with the requirements for toilet facilities outlined above. Existing food service establishments must also meet the requirements for toilet facilities outlined above if there is or has been a sufficient increase in the number of seats or if the nature of the food service operation changes such that additional toilet facilities would be needed. Fixtures shall be of readily cleanable sanitary design. Toilet facilities shall be kept clean, in good repair and free from objectionable odors. Toilet tissue shall be provided. Easily cleanable receptacles shall be provided for waste materials and such receptacles in toilet rooms for women shall be covered. Toilet rooms shall be completely enclosed and shall have tight-fitting, self-closing doors. Such doors shall not be left open except during cleaning or maintenance. Handwashing signs shall be posted in each toilet room used by employees.

(5) Handwashing facilities – Each food service establishment shall be provided with adequate, readily accessible, conveniently located lavatories equipped with hot and cold running water, hand cleansing soap or detergent and individual single use sanitary towels or a heated-air hand drying devices in accordance with provisions of the applicable plumbing authority or, where no plumbing code has been adopted locally, with Chapter 64E-10, F.A.C. Handwashing facilities shall not be used for any purpose other than handwashing.

(a) Lavatories shall be located in or immediately adjacent to all toilet rooms. At least one employee handwashing facility shall be located within each food preparation area.

(b) Employee handwashing facilities shall be installed in rooms or in areas where mechanical dishwashing machines operate that are isolated or remote from food preparation areas.

(c) Lavatories, soap dispensers, hand-drying devices and all other components of the handwashing facilities shall be kept clean and in good repair. Handwashing signs shall be posted at each handwashing facility.

(d) Hot and cold running water under pressure shall be provided at all employee handwashing sinks.

(6) Garbage and rubbish disposal.

(a) All garbage and rubbish containing food wastes shall, prior to disposal, be kept in leakproof, nonabsorbent containers which shall be kept covered with tight fitting lids; provided that such containers need not be covered when stored in a special vermin proofed room or in a closed food waste refrigerator. Containers which do not have tight fitting vermin proof lids may be used only if garbage is first placed in plastic bags or wet-strength paper bags which are securely tied closed. All other rubbish shall be stored in an approved manner. The rooms, enclosures, areas and containers used shall be adequate for the storage of all food wastes and rubbish which accumulates between periods of removal.

(b) Garbage and refuse containers, compactors and dumpsters located outside shall be stored on or above a smooth surface of nonabsorbent material such as concrete that is kept clean and maintained in good repair. If a compactor system is used for the storage of garbage, and the garbage is not stored in a self-contained and leak proof system, the compactor shall be placed on a concrete pad which is graded to drain into a sanitary sewer system.

(c) Adequate cleaning facilities shall be provided and each container, room or area shall be thoroughly cleaned after the emptying or removal of garbage and rubbish. Waste water from such cleaning operations shall be disposed of as sewage. Food waste grinders, if used, shall be suitably constructed and shall be installed in accordance with provisions of the applicable plumbing authority. All garbage and rubbish shall be removed from the food establishment premises with sufficient frequency to prevent nuisance conditions and shall be disposed of in accordance with provisions of Chapter 62-701, F.A.C.

(7) Vermin control – Effective control measures shall be taken to protect against the entrance into the food establishment, and the breeding or presence on the premises of rodents, flies, roaches and other vermin. All buildings shall be effectively rodent-proofed, free of rodents and maintained in a rodent-proof and rodent-free condition. All openings to the outside air, including windows, doors, skylights, transoms, intake and exhaust ducts shall be effectively protected against the entrance of flies and other flying insects by self-closing doors which open outward, closed windows, screening, controlled air currents or other effective means. Screening material shall not be less than 16 mesh to the inch or equivalent and screens for windows, doors, skylights, transoms and other openings to the outside air shall be tight fitting and free of breaks. Insecticides or rodenticides, when used, shall be used in full compliance with Chapter 5E-14, F.A.C.

Rulemaking Authority 381.006, 381.0072 FS. Law Implemented 381.006, 381.0072 FS. History–New 1-1-77, Amended 1-6-81, Formerly 10D-13.27, Amended 2-21-91, 5-12-92, Retained here and Transferred to 7C-4.014, Formerly 10D-13.027, Amended 3-15-98, 7-14-03.