69A-46.041 Inspection, Testing and Maintenance Requirements for Fire Protection Systems.

The contractor I or II shall submit in writing to the Regulatory Licensing Section the names, addresses, and evidence of NFPA 25 training of all individuals in his or her employ that are performing inspections of fire protection systems. In addition, the licensed contractor I or II shall submit a full face current color passport photograph of each inspector along with a copy of the inspector’s current driver’s license or identification card issued by the Florida Department of Highway Safety and Motor Vehicles. The contractor shall not allow any individual to perform inspections under his or her certificate until that individual has been listed with the Regulatory Licensing Section. The Regulatory Licensing Section shall issue a identification card to each inspector. The identification card is not a license. The contractor shall be responsible for each listed individual’s inspections until he or she has requested in writing that the Regulatory Licensing Section delete the individual from his or her list of inspectors. The licensed fire protection system contractor shall notify the Regulatory Licensing Section, in writing, of an inspector leaving his or her employ within fifteen days of the termination. An inspector photo identification card of an individual leaving the employ of a contractor becomes void and inoperative on the date of departure.

(1) A Fire Protection Contractor, contracting to perform inspecting, testing, and maintenance service on a fire protection system shall comply with the requirements of the applicable NFPA standard as adopted in Rule Chapter 69A-3, F.A.C.

(2) Each system that has been inspected, tested, or maintained by a fire protection contractor, or his or her designated inspector, shall have a record tag of durable and weather resistant material placed on the riser or control device. The tag at “Figure A” shall include the following:

(a) Name, address and contractor license number of company.

(b) Date of inspection and type of inspection.

(c) Inspected by __________.

(d) The tag shall state “For more information see the inspection report.”

(e) The tag shall state “Do not remove by order of the State Fire Marshal.”

(f) The tag shall be approximately 3 1/2 inches by 5 1/2 inches.

(3) The contractor shall maintain in his or her file all records of any fire protection system having been serviced.

(4) These records shall be made available to the State Fire Marshal upon request.

(5) The contractor or the designated inspector shall complete in detail the inspection reports as required in NFPA 25, as adopted in Rule Chapter 69A-3, F.A.C., that outlines all points of the inspection, test, and maintenance as required by the applicable NFPA standards. A copy of which shall be provided to the owner at the completion of each inspection performed.

(6) The inspection report shall include detailed explanation of any deficiencies. The report shall indicate if the inspection is a weekly, monthly, quarterly or annual inspection. The inspection report shall include the name of the registered inspector, the inspector registration number, signature, the date and time of inspection, and the signature of the owner or the owner’s representative.

SEE FLORIDA ADMINISTRATIVE CODE FOR “FIGURE A”

Specific Authority 633.01 FS. Law Implemented 471.025, 553.79(6), 633.065, 633.547(2)(e) FS. History–New 10-20-93, Amended 11-21-01, Formerly 4A-46.041.