# CHAPTER 40A-44

# REGULATION OF AGRICULTURAL AND FORESTRY SURFACE WATER MANAGEMENT PROJECTS

# 40A-44.011	Policy and Purpose

# 40A-44.021	Definitions

# 40A-44.031	Implementation (Repealed)

# 40A-44.041	Permits Required

# 40A-44.051	Exemptions

# 40A-44.052	Authorization for Certain Forestry Projects

# 40A-44.091	Processing of Permits

# 40A-44.101	Content of Application

# 40A-44.142	Headgates, Valves, and Measuring Devices

# 40A-44.143	Abandonment (Repealed)

# 40A-44.201	Permit Processing Fee

# 40A-44.301	Conditions for Issuance of Permits

# 40A-44.321	Duration of Permit

# 40A-44.331	Modification of Permits

# 40A-44.341	Revocation of Permits

# 40A-44.351	Transfer of Permits

# 40A-44.381	Limiting Conditions

# 40A-44.411	Completion Report

# 40A-44.451	Emergency Authorization

# 40A-44.461	Inspections (Repealed)

# 40A-44.901	Forms

## 40A-44.011 Policy and Purpose.

The purpose of these rules is to implement the expressed policy of the Northwest Florida Water Management District and the State of Florida to assure that agricultural and forestry projects relating to the management, storage, and drainage of surface waters will not be harmful to the water resources, and will provide for the safety of life and property. The following constitutes an expression of the objectives of the District with regard to its permitting powers.

(1) It shall be the objective of the District to encourage sound agricultural and forestry water management practices in a manner which provides for the conservation of the District’s water resources.

(2) It shall be the objective of the District to provide that the discharge to waters of the State from agricultural and forestry surface water management projects meet the water quality provisions of Chapters 62-302 and 62-4, F.A.C.

(3) It shall be the objective of the District to ensure that any dam, impoundment, reservoir, appurtenant work, or works under permit does not create a hazardous condition which might threaten lives or property.

(4) It shall be the objective of the District to ensure that the waters within the District are not depleted, restricted, or otherwise impaired by artificial means unless permitted by the District.

(5) It shall be the objective of the District to ensure the protection and preservation of wetlands and other water-dependent natural systems.

Rulemaking Authority 373.044, 373.113, 373.418 FS. Law Implemented 373.413, 373.416, 373.418, 373.426 FS. History–New 10-1-84, Amended 7-1-92.

## 40A-44.021 Definitions.

(1) “Best management practices for agriculture” means those conservation, management and operational practices identified for agriculture as best for reducing pollution and identified in the Florida Department of Agriculture and Consumer Services Best Management Practices adopted under Division 5M, F.A.C.

(2) “Best management practices for forestry” means those conservation, management and operational practices identified for silviculture as best for reducing pollution and identified in the Florida Department of Agriculture and Consumer Services Best Management Practices adopted under Chapter 5I-6, F.A.C.

(3) “Class I Waters” means those surface waters listed pursuant to Rule 62-302.400, F.A.C.

(4) “Endangered Species” means those plants, fish and wildlife listed pursuant to paragraph 5B-40.0055(2)(a) and Rule 68A-27.003, F.A.C., Section 581.185(2)(b), F.S., 50 CFR 17.11, and 50 CFR 17.12.

(5) “Existing Facility” means a dam, impoundment, reservoir, appurtenant work, or works that were constructed under authorization by the District, or constructed before October 1, 1984, and that has been used and maintained within the 3 years prior to application for a permit under subsection 40A-44.301(4), F.A.C.

(6) “Farm Pond” means a pond located on a farm and used for farm purposes.

(7) “Farm Purposes” means and includes farm water supply, erosion control, fish and wildlife enhancement or flood control.

(8) “Farm Water Supply” means water used for irrigation, livestock watering, fire protection or general on-farm use.

(9) “Outstanding Florida Waters” means those surface waters listed pursuant to Rule 62-302.700, F.A.C.

(10) “Projects” means one or more agricultural or forestry activities resulting in the construction, operation and maintenance, alteration, modification or abandonment of structures or works for the sole or predominant purpose or effect of impounding, draining, or obstructing surface waters.

(11) “Species Of Special Concern” means those fish and wildlife listed pursuant to Rule 68A-27.005, F.A.C.

(12) “Steephead Ravines” means those highly distinctive stream valleys as described in “A Ecological Characterization of the Florida Panhandle,” U.S. Fish and Wildlife Service Biological Report 88(12), U.S. Fish and Wildlife Service, 1988, which is hereby incorporated by reference. A copy of which can  be obtained from http://www.flrules.org/Gateway/Reference.asp?No=Ref-02991, or the District’s website www.nwfwater.com.

(13) “Threatened Species” means those plants, fish and wildlife listed pursuant to paragraph 5B-40.0055(2)(b), F.A.C., 50 CFR 17.11, and 50 CFR 17.12.

(14) “Wetlands” means those areas that are inundated or saturated by surface or ground water with a frequency sufficient to support, and under normal circumstances do or would support, a prevalence of vegetation or aquatic life that requires saturated or seasonally saturated soil conditions for growth and reproduction, such as swamps, marshes, bayheads, cypress ponds, sloughs, wet prairies, wet meadows, river overflows, mud flats and natural ponds.

Rulemaking Authority 373.113, 373.418 FS. Law Implemented 373.413, 373.416, 373.418, 373.426 FS. History–New 10-1-84, Amended 7-1-92, 3-30-94, 8-6-13.

## 40A-44.031 Implementation.

Rulemaking Authority 373.044, 373.171 FS. Law Implemented 373.409, 373.413, 373.416, 373.426 FS. History–New 10-1-84, Repealed 7-1-98.

## 40A-44.041 Permits Required.

(1) Unless expressly exempted by law or District rule, a surface water management permit must be obtained, pursuant to this chapter, from the District to construct, alter, operate, maintain, or abandon any dam, impoundment, reservoir, appurtenant work or works associated with agricultural or forestry projects.

(2) The District issues three types of agricultural and forestry surface water management permits: general surface water management permits, individual surface water construction permits, and individual operation and maintenance permits.

(a) General Surface Water Management Permits. This permit provides for the construction, maintenance, and operation of a facility. A general permit is applicable for projects:

1. Within a watershed which contains less than 640 acres above (upstream of) the project’s point of discharge, or

2. Which could impound water by a dam which is less than ten feet in height from the natural bed of the water course at the downstream toe of the barrier, as determined by the District, or which has an impounding capacity of less than fifty (50) acre-feet, and

3. Has either singly or cumulatively, a minimal adverse impact on the water resources of the District.

(b) Individual Surface Water Construction Permits. A permit is applicable for all projects which are not exempt, which are not eligible for a general permit, or which are not otherwise authorized activities pursuant to this chapter.

(c) Operation and Maintenance Permits. A permit for operation and maintenance of any dam, impoundment, reservoir, appurtenant work or works is required for permitted projects under paragraph 40A-44.041(2)(b), F.A.C.

Rulemaking Authority 373.044, 373.113, 33.418 FS. Law Implemented 373.118, 373.406, 373.413, 373.416, 373.418, 373.426 FS. History–New 10-1-84, Amended 8-1-89, 7-1-92, 7-1-98, 8-6-13, 3-27-19.

## 40A-44.051 Exemptions.

(1) Activities specified in Section 373.406, F.S., are exempt from this chapter.

(2) Projects permitted pursuant to this chapter are exempted from the provisions of Chapter 62-330, F.A.C., as long as the land served by the project continues to be used for agriculture or forestry.

Rulemaking Authority 373.044, 373.113, 373.171, 373.418, 373.813 FS. Law Implemented 373.416, 373.406, 373.413, 373.418, 373.426, 403.813 FS. History–New 10-1-84, Amended 3-27-17.

## 40A-44.052 Authorization for Certain Forestry Projects.

(1) Authorization is hereby granted, subject to the general and specific conditions of this section, to any person who is engaged in forestry operations to conduct the minor works described below:

(a) Culvert placement, replacement and maintenance, in streams of less than 10 cubic feet per second average discharge at the culvert location or streams draining less than 10 square miles, except for culverts associated with low water crossings, provided that construction does not cause scour in the downstream waters or increase the velocity of the water downstream.

(b) Bridge construction, replacement and maintenance for structures up to 400 feet in length and two lanes or less in width supported by pilings or trestles where the effects of pollutants discharged into open waters can be minimized.

(c) Construction and maintenance of low water crossings (hard surface crossings over which water flows during storm events or immediately thereafter) provided construction does not cause scour in the downstream waters or increase the velocity of the water downstream.

(d) Temporary stream channel diversions necessary to complete projects detailed in paragraphs (a), (b) and (c), above, provided the area used for the temporary diversion is restored to its previous contours and elevations.

(e) Channel clearing and shaping to facilitate maximum hydraulic efficiency of designed structure detailed in paragraphs (a), (b) and (c), above.

(f) Site preparation and access roads on existing forestry lands including any ditch constructed or maintained with a total cross-sectional area at the outfall of less than 35 square feet when a berm or buffer zone of vegetation separates the site being prepared and the open water. Where an access road crosses open water, the crossing construction shall be in accordance with paragraph (a), (b), (c), (d) or (e), above.

(2) Prior to the construction, replacement, or maintenance of a minor forestry work authorized under this section, notice shall be given to the District as follows:

(a) A completed Forestry Authorization Notification Form, No. A44-F, effective 7-1-92, which is hereby incorporated by reference, and copies of which can be obtained from http://www.flrules.org/Gateway/Reference.asp?No=Ref-02969, the District office identified below, or by electronic submittal at the District’s website www.nwfwater.com, shall be submitted to the District no less than two (2) working days prior to the commencement of work. For notification forms mailed to the District, the postmark date shall be the date of submittal.

(b) Emergency notification will be allowed under this section provided the District receives a completed Forestry Authorization Notification Form or is notified by telephone prior to the commencement of work. Telephone notification shall be followed by submittal of a completed Forestry Authorization Notification Form no less than two (2) working days after such telephone notification. A serious set of unforeseen or unforeseeable circumstances must exist to create an emergency. Mere carelessness or lack of planning on the part of the applicant shall not be sufficient grounds to warrant the granting of emergency authorizations.

(c) All forestry authorization notifications shall be made to the District office identified below:

Northwest Florida Water Management District

DeFuniak Springs Field Office

700 US Highway 331 S

DeFuniak Springs, FL 32435

(d) The person seeking an authorization, in lieu of an individual project notification, may submit a yearly work plan authorization request. The required plan shall be filed with the DeFuniak Springs Service Office and shall identify the type, location and implementation timetable for each proposed minor work authorized under the provisions of this section. Yearly work plans shall be submitted thirty (30) days prior to the commencement of the implementation of the identified works and may be modified under individual project authorizations.

(3) This authorization shall be subject to the general conditions of subsection 40A-44.301(2), F.A.C, and the following specific conditions:

(a) Notice has been filed with the District as provided for in subsection 40A-44.052(2), F.A.C.

(b) The person shall use Best Management Practices for Forestry as defined in subsection 40A-44.021(2), F.A.C.

(c) The person shall stabilize fill areas and stream banks disturbed by the activity by revegetation or riprap as appropriate.

(d) The person shall limit stream channel relocation to streams which have an average annual discharge of 10 cubic feet per second or less. The length of relocated channels or those significantly altered shall be limited to 200 feet per stream. A stream channel shall be altered only when such a measure will reduce the long term adverse water quality impacts and will maintain or restore the stream’s natural hydraulic capability.

(e) The person shall limit bridge construction to those bridges spanning bank to bank with no causeway approaches in the floodplain unless there are sufficient culverts in the causeway to prevent downstream scour or increase in the velocity of the water downstream. This limitation does not apply to maintenance of existing bridges or to the construction of temporary log and pole bridges.

(f) The person shall limit crossings of any particular stream to an average of one every 1/2 mile.

(4) This authorization does not apply to activities which convert waters in the state to uplands by draining the land, site preparation or other practices designed to bring an area not used for forestry into such use or forest land into other uses. However, it shall apply to activities on areas lying fallow as part of a conventional rotation cycle of an established forestry operation. An operation ceases to be established when the area on which it was conducted has been converted to another use or has lain idle more than 5 years.

(5) If at any time the District discovers that an Authorization has been used to conduct minor forestry works which do not qualify for an Authorization under this section, or an authorized activity is not being conducted in accordance with the conditions described in this section, the District shall either require application for a permit pursuant to Chapter 62-330, 40A-6 or 40A-44, F.A.C., or shall take administrative or judicial enforcement action, or any combination thereof, as it deems appropriate.

Rulemaking Authority 373.044, 373.113, 373.418 FS. Law Implemented 373.118, 373.406(5), 373.413, 373.416, 373.426 FS. History–New 10-1-84, Amended 9-15-86, 8-1-89, 7-1-92, 8-6-13, 3-27-17.

## 40A-44.091 Processing of Permits.

(1) Individual surface water construction permits and general surface water management permits shall be processed according to the provisions of chapter 40A-1, F.A.C., and require approval by the Executive Director or his/her designee.

(2) General surface water management permits for projects other than impoundments constructed in waters in the State shall be processed in accordance with all applicable provisions of Chapter 40A-1, F.A.C., and shall be issued by the Executive Director or Executive Director’s designee after the submitted application is determined to be complete and meets the requirements of this chapter.

(3) Permit application notices shall be processed in accordance with the provisions of Chapter 40A-1, F.A.C., and Sections 373.116 and 373.413(3), F.S.

Rulemaking Authority 373.044, 373.113, 373.418 FS. Law Implemented 373.116, 373.118, 373.406, 373.413, 373.4141, 373.416, 373.426 FS. History–New 10-1-84, Amended 7-1-92, 7-1-98, 8-6-13, 3-27-17, 3-27-19.

## 40A-44.101 Content of Application.

(1) Applications for permits required by this chapter shall include:

(a) Form No. A44-A, Surface Water Management Permit Application, amended 7-1-98, which is hereby incorporated by reference. A copy of which can be obtained by contacting the District, or online at http://www.flrules.org/Gateway/Reference.asp?No=Ref-02964 or the District’s website www.nwfwater.com;

(b) The information required in Section 373.413(2), F.S.;

(c) Drawings, calculations, and engineering details sufficient to define the nature, scope, intent and functioning of the proposed project. This information shall include the following:

1. The area of innundation depicted on a topographic map,

2. Hydraulic calculations; and,

3. Flow characteristics;

(d) Information supporting the agricultural status of the property which shall include:

1. A Soil and Water Conservation District approved conservation plan, or a notice of intent to participate in the appropriate Best Management Practices program offered by the Florida Department of Agriculture and Consumer Services,

2. A copy of the receipt of application for agricultural classification of the property (Green Card); and,

3. A Farm Service Agency (FSA) farm number.

4. An Affidavit of Agricultural Status, Form A44-E, effective 7-1-92, which is hereby incorporated by reference, copies of which can be obtained by contacting the District or online at http://www.flrules.org/Gateway/Reference.asp?No=Ref-02968, or the District’s website www.nwfwater.com, may be substituted for the ASCS farm number and verification of agricultural classification. In areas of changing land uses, from agricultural to other uses, an affidavit is required;

(e) The name, address and zip code of all property owners adjacent to the affected water body that are immediately downstream of the property upon which the proposed project will take place;

(f) An inventory of the wetland impacts of the project which shall include: total wetlands on site, wetlands permanently lost, wetlands temporarily disturbed, wetlands created, wetlands improved, and other site specific wetland information;

(g) An inventory of endangered or threatened species, and species of special concern known to occur on the site, as listed pursuant to Rules 5B-40.0055, 68A-27.003, and 68A-27.005, F.A.C.; Section 581.185(2)(b), and (h), F.S.; and 50 CFR 17.11-12; and,

(h) Other site specific information as necessary to support the reasonable assurances determination pursuant to subsection 40A-44.301(2), F.A.C.

(2) The application must be signed by the owner or his authorized agent, if applicable.

(3) The District shall require the applicant to submit other pertinent information deemed necessary for evaluating the application.

Rulemaking Authority 373.044, 373.113, 373.418 FS. Law Implemented 373.116, 373.118, 373.406(5), 373.413, 373.416, 373.426 FS. History–New 10-1-84, Amended 7-1-92, 8-6-13, 3-27-17.

## 40A-44.142 Headgates, Valves, and Measuring Devices.

(1) The owner of any dam, impoundment, reservoir, appurtenant work, or works subject to this chapter may be required, after notice and hearing by the Governing Board, to install and maintain a substantial and serviceable headgate or valve at the point where the water is discharged or diverted, and shall, if required by the Governing Board, install a measuring device which will adequately measure the water at a point designated by the Governing Board for the purpose of investigating any effects of the structure.

(2) If any owner shall not have constructed or installed such headgate, valve, or such measuring device within 60 days after the Governing Board has ordered its construction, the Governing Board shall have constructed or installed such headgate, valve, or measuring device, and the costs of installing the headgate, valve, or measuring device shall be a lien against the owner’s land upon which such installation takes place until the Governing Board is reimbursed, with reasonable interest and attorney’s fees, for its costs.

(3) No person shall alter or tamper with a measuring device so as to cause it to register other than the actual amount of water diverted, discharged, or taken.

(4) For the purpose of safety and maintenance, any new dams, impoundments, or appurtenant works meeting the requirements of Rule 40A-44.041, F.A.C., shall be required to have installed and maintained a substantial and serviceable headgate or valve at the point where the water is diverted or discharged.

Rulemaking Authority 373.044, 373.113, 373.418, 373.436 FS. Law Implemented 373.409, 373.436 FS. History–New 10-1-84, Amended 8-6-13.

## 40A-44.143 Abandonment.

Rulemaking Authority 373.044, 373.113, 373.418 FS. Law Implemented 373.426 FS. History–New 10-1-84, Repealed by Section 3, Chapter 2012-31, Laws of Florida, 5-27-12.

## 40A-44.201 Permit Processing Fee.

A non-refundable permit processing fee shall be filed with the District, at the time of application submittal, according to the following fee schedule:

Type of Permit	Fee

(1)	General Surface Water Management Permit	25.00

(2)	Individual Surface Water Construction Permit

Watershed less than 4 square miles	250.00

Watershed 4 square miles or larger	500.00

(3)	Operation and Maintenance Permit	No Fee

Rulemaking Authority 373.044, 373.113, 373.418 FS. Law Implemented 373.109 FS. History–New 10-1-84, Amended 1-1-90, 7-1-98, 3-27-19.

## 40A-44.301 Conditions for Issuance of Permits.

(1) The District shall not issue a permit for a new agricultural water management system impoundment or a farm pond impoundment within:

(a) An Outstanding Florida Water unless the applicant provides reasonable assurance that the proposed activity will be clearly in the public interest per Section 373.414, F.S.; or

(b) A stream which has as its headwaters:

1. A steephead ravine, or

2. Tributary streams which are discharging from steephead ravines.

(2) The District, in deciding whether to grant, conditionally grant, or deny a permit under this chapter, will determine whether information submitted by the applicant, or otherwise available to the District, provides reasonable assurance that the surface water project:

(a) Provides adequate flood protection and drainage;

(b) Will not cause unacceptable water quality and quantity impacts on waters and adjacent lands regulated pursuant to Chapter 373, F.S.;

(c) Will not cause discharges which result in any violation, in waters of the State, of the standards and criteria of Chapters 62-302 and 62-4, F.A.C.;

(d) Will not cause unacceptable adverse impacts on surface and ground-water levels and flows;

(e) Will not cause unacceptable adverse environmental impacts to natural resources, fish, and wildlife;

(f) Can be effectively operated and maintained;

(g) Will not endanger life, health, or safety, or adversely affect property;

(h) Is consistent with generally accepted engineering standards, design and safety practices and Best Management Practices for local conditions as defined in this chapter;

(i) Is consistent with the overall objectives of the District and State Water Policy as established in Section 373.016, F.S., rule 40A-44.011 and Chapter 62-40, F.A.C.

(3) For new projects, the District will assume that the applicant has demonstrated the reasonable assurances required in subsection 40A-44.301(2), F.A.C., if the project design, construction, operation and maintenance plans are determined to meet or incorporate the following applicable standards, and if the permit can be conditioned, as provided by Rule 40A-44.381, F.A.C., to provide for specific project characteristics and permit administration consideration:

(a) The project has not been sited within a steephead ravine(s), and is not contrary to the public interest per Section 373.414, F.S.;

(b) The project has been sited, sized and designed to avoid impacts to endangered or threatened species;

(c) The project has been sited, sized and designed to minimize impacts to species of special concern, existing natural resources, fish, and wildlife;

(d) Erosion control projects have been sited in uplands;

(e) The project utilizes appropriate Best Management Practices and implements a Soil and Water Conservation District approved conservation plan, which provides the water quality assurances required in paragraphs 40A-44.301(2)(b) and (c), F.A.C.;

(f) Outfalls are designed to minimize erosion and, when necessary, to provide energy dissipation and aeraton of discharged water;

(g) Stream management and protection zones are provided above and below authorized structures within the property owned by the permittee;

(h) Adequate erosion and sediment control devices are utilized during construction to prevent downstream violations of water quality;

(i) The project incorporates site specific and applicable engineering standards, design, operation and maintenance measures to provide for the physical safety and stability of the facility;

(j) The project incorporates site specific and applicable design, operation and maintenance measures to provide for the protection and conservation of natural resources;

(k) Impoundment design, construction, operation and maintenance incorporates the following criteria and standards:

1. Design of principal and emergency spillways to pass flood events in a manner that will not threaten life or property. At a minimum, principal and emergency spillways must be designed to pass the appropriate 2- and 25-year, 24 hour storm event. Impoundments with a hazard classification greater than low may have to be designed to pass greater storm events;

2. The project has been sited to minimize cumulative impacts caused by multiple impoundments within a stream by providing separation between impoundments for recovery of stream function and value;

3. The average depth of new impoundments does not exceed 6 feet;

4. Installation of deep water or mid-level water release when the deepest part of an impoundment exceeds 10 feet. Design of these types of release must provide for the prevention of bottom scouring or sediment release;

5. New impoundment surface water area at normal pool is not greater than 6 acres;

6. Impoundment design and operation provides for water level fluctuation and for full drawdown;

7. Creation of wetland littoral zones to water depths of 3 feet. Organic or mucky soils excavated during construction of permitted structures shall be stockpiled and used in the creation of littoral zones;

8. Location of borrow pits in uplands or in other locations which maximize littoral zone creation;

9. Cutting and removal of trees and shrubs from the area of innundation to minimize nutrient imbalance in the impoundment. Disturbance to soils and topography shall be minimized; and,

10. Upland buffer zones are utilized to provide runoff filtration, water quality enhancement, and to control erosion.

(4) For projects involving the reconstruction, repair or alteration of existing facilities, as defined in subsection 40A-44.021(5), F.A.C., the District will assume that the applicant has demonstrated the reasonable assurances required in subsection 40A-44.301(2), F.A.C., if the project design, construction, operation and maintenance plans are determined to meet or incorporate the following standards and criteria, and if the permit can be conditioned, as provided by Rule 40A-44.381, F.A.C., to provide for specific project characteristics and permit administration consideration:

(a) The project has incorporated all applicable standards in subsection 40A-44.301(3), F.A.C.;

(b) Any proposed expansion of the storage capacity of an existing impoundment will be for safety or primarily for irrigation or livestock watering. Expansion for irrigation or livestock watering shall be sized to provide the water needs of these uses;

(c) The proposed reconstruction, repair or alteration is designed to avoid impacts to endangered or threatened species, and species of special concern;

(d) The proposed reconstruction, repair or alteration is designed to minimize impacts to existing natural resources, fish, and wildlife;

(e) The project incorporates site specific and applicable engineering standards, design, operation and maintenance measures to provide for the physical safety and stability of the facility; and,

(f) The project incorporates site specific and applicable design, operation and maintenance measures to provide for the protection and conservation of natural resources.

(5) For projects which do not meet or incorporate the standards and criteria in subsections 40A-44.301(3) and (4), F.A.C., the District, in deciding if the reasonable assurances of subsection 40A-44.301(2), F.A.C., can be met, will consider the following additional criteria:

(a) Whether the project will degrade Outstanding Florida Waters, Class I waters, or steephead ravines;

(b) Whether the project, if a stream impoundment, will be primarily used for irrigation or livestock watering and has been sized to provide the water needs of these uses;

(c) Whether the project will result in violations of State water quality standards and criteria pursuant to Chapters 62-302 and 62-4, F.A.C.;

(d) Whether the project will adversely affect natural resources, fish, and wildlife, including endangered or threatened species and species of special concern;

(e) Whether the project will adversely affect fishing or recreational values, or marine productivity in the vicinity and downstream of the project;

(f) Whether the project will result in, or contribute to, cumulative impacts which will degrade waters in the State. In determining whether unacceptable cumulative impacts may occur, the District will consider:

1. The impact of the project for which the permit is sought; and,

2. The impact of projects which are existing or under construction or for which permits have been sought.

(6) If a permit application does not provide the reasonable assurances or meet the design and evaluation criteria set forth in subsections 40A-44.301(2)-(5), F.A.C., the District will consider proposals of other measures that can be taken to mitigate the adverse impacts which may be caused by the project.

(7) Project plans and specifications for permits required under:

(a) Paragraph 40A-44.041(2)(a), F.A.C., must be signed and sealed by a professional engineer registered in the State of Florida pursuant to Chapter 471, F.S., or are in accordance with the United States Department of Agriculture Natural Resources Conservation Service Standards and Specifications and have been approved by a Soil and Water Conservation District created pursuant to Chapter 582, F.S.

(b) Paragraph 40A-44.041(2)(c), F.A.C., must be signed and sealed by a professional engineer registered in the State of Florida, pursuant to Chapter 471, F.S., or are in accordance with the United States Department of Agriculture Natural Resources Conservation Service Standards and Specifications and have been approved by a Soil and Water Conservation District created pursuant to Chapter 582, F.S. However, plans and specifications for any dam exceeding 25 feet in height or impounding more than 50 acre-feet of water must be signed and sealed by a professional engineer registered in the State of Florida, pursuant to chapter 471, F.S.

Rulemaking Authority 373.044, 373.113, 373.414, 373.418 FS. Law Implemented 373.118, 373.406(5), 373.413, 373.416, 373.426 FS. History–New 10-1-84, Amended 7-1-92, 3-27-19.

## 40A-44.321 Duration of Permit.

(1) Unless revoked or otherwise modified, the duration of a permit pursuant to this chapter is:

(a) Five years, for a construction permit;

(b) Perpetual, for an operation and maintenance permit, except any operation and maintenance permit on an existing facility shall automatically expire when a new operation and maintenance permit or abandonment permit is issued for that same facility.

(2) Construction permits expire automatically unless the permittee requests an extension before the expiration date.

Rulemaking Authority 373.044, 373.113, 373.418 FS. Law Implemented 373.118, 373.406(5), 373.413, 373.416, 373.426 FS. History–New 10-1-84, Amended 8-6-13, 3-27-19.

## 40A-44.331 Modification of Permits.

An application for modification of a surface water management permit shall be processed in accordance with this rule, unless otherwise revoked, suspended or expired.

(1) Applications to modify Individual Surface Water Construction or Individual Operation and Maintenance permits shall be made;

(a) By formal application and reviewed using the same criteria as new applications, pursuant to Rules 40A-44.101 and 40A-44.301, F.A.C., or

(b) By letter, provided the requested modification does not:

1. Substantially alter the permit authorization,

2. Increase the authorized discharge,

3. Impact the environmental features of the project,

4. Decrease the required retention/detention,

5. Decrease any required flood control elevations for roads or buildings, and

6. Exceed water quality standards at points of discharge as provided in Chapters 62-302 and 62-4, F.A.C.

(2) Applications to modify a General Surface Water Management Permit shall be made:

(a) In accordance with Rules 40A-44.041, 40A-44.101 and 40A-44.301, F.A.C., or

(b) By letter providing the requested modification does not exceed the conditions of paragraph 40A-44.331(2)(b), F.A.C.

Rulemaking Authority 373.044, 373.113, 373.418 FS. Law Implemented 373.118, 373.406(5), 373.413, 373.416, 373.426, 373.429 FS. History–New 10-1-84, Amended 7-1-98, 3-27-17, 3-27-19.

## 40A-44.341 Revocation of Permits.

(1) Certain violations of this chapter shall result in the revocation of the permit authorization in whole or in part. A permit may also be revoked under any of the following circumstances:

(a) The permittee or his agent has committed any of the acts enumerated in subsections 40A-1.205(1) or (2), F.A.C., or

(b) The permittee has not proceeded in a timely fashion to construct the authorized facilities and the permit has automatically expired pursuant to Rule 40A-44.321, F.A.C.

(2) The conversion of a project to any use other than forestry or agriculture shall result in the revocation of the permit and be subject to the applicable provisions of Chapter 403, F.S., and Chapter 62-330, F.A.C.

(a) The revocation of a permit under this provision shall require the removal of the surface water management facility, restoration of topography, and the stabilization of the site to prevent water quality impacts and erosion. The removal of the facility shall not be required, if the permittee provides for the redesign of the facility and is granted authorization by the District to alter the facility to meet construction, safety, and water quality standards suitable for the intended use.

(b) The permittee shall be required to dewater the facility immediately and maintain the facility dewatered until the necessary permit and authorizations are obtained and the facility is altered or removed.

(3) The partial conversion of a project’s watershed upstream from the project’s site, under the initial ownership or control of the permittee, to uses other than forestry or agriculture shall require the filing of a permit modification according to the provisions of Rule 40A-44.331, F.A.C.

(a) The permit modification application shall address the new hydraulic characteristics of the facility and provide for its redesign and alteration to meet construction, safety and water quality standards suitable for the intended uses.

(b) The permittee shall be required to undertake any required alteration construction prior to the partial watershed conversion.

Rulemaking Authority 373.044, 373.113, 373.418 FS. Law Implemented 373.423, 373.429 403.927(3) FS. History–New 10-1-84, Amended 8-1-89, 7-1-92, 7-1-98, 8-6-13, 3-27-17.

## 40A-44.351 Transfer of Permits.

(1) Upon timely notice that a permitted project or lands on which the facility is located has been sold or otherwise transferred to a new owner, the permit shall be transferred to a new owner. Until properly transferred the original permittee shall remain responsible for the proper operation and maintenance of the facility.

(2) If not properly transferred within 30 days of the sale of the facility or lands on which the facility is located, the permittee shall inform the transferee of the use limitations associated with the permitted facility. The transferee shall execute an affidavit acknowledging his awareness of the conditions and restrictions associated with the permit issued by the District.

(3) Requests for transfer of permit shall be made on Form No. A44-D, Acceptance of Transfer of Permit Issued, effective 7-1-92, amended 03/2017, which is hereby incorporated by reference, copies of which can be obtained by contacting the District or online at http://www.flrules.org/Gateway/reference.asp?No=Ref-08040, or the District’s website www.nwfwater.com.

Rulemaking Authority 373.044, 373.113, 373.418 FS. Law Implemented 373.413, 373.416(2), 373.418, 373.426 FS. History–New 10-1-84, Amended 8-1-89, 7-1-92, 8-6-13, 3-27-17.

## 40A-44.381 Limiting Conditions.

(1) The Board will impose on any permit granted under this chapter such reasonable conditions as are necessary to assure that the permitted operation will be consistent with the overall objectives of the District and will not be harmful to the water resources of the District.

(2) In addition to project specific special conditions, the following limiting conditions will be attached to any permit issued pursuant to this chapter.

(a) The permittee shall prosecute the work authorized in a manner so as to minimize any adverse impact of the works on fish, wildlife, natural environmental values, and water quality. The permittee shall institute necessary measures during the construction period, including required compaction of any fill material placed in or around newly installed structures, to reduce erosion, turbidity, nutrient loading and sedimentation in the receiving waters.

(b) The authorized facility shall not be determined fully complete, and the Operation and Maintenance Permit shall not become effective, until the “As-Built Certification and Completion Report” required pursuant to subsection 40A-44.301(7) and Rule 40A-44.411, F.A.C., is submitted to the District, and the District has determined the project to have been constructed in accordance with the approved design and any permit conditions stipulated in the construction authorization. The Permittee shall submit to the District a properly executed “As-Built Certification and Completion Report” within 30 days of the completion of the permitted project.

(c) Discharges during construction shall be made only through the facilities authorized by this permit. Water discharged from the project shall be through structures having a mechanism suitable for regulating upstream water stages. Stages may be subject to operating schedules satisfactory to the District.

(d) The permit does not convey to the permittee any property right nor any rights or privileges other than those specified in the permit and Chapter 40A-44, F.A.C.

(e) The permittee, by acceptance of this permit, agrees to its terms and conditions, and agrees to hold and save the District harmless from any and all damages, claims, or liabilities which may arise by reason of the construction, operation, maintenance or use of any facility authorized by the permit.

(f) Prior to any dewatering, plans shall be submitted to the District for approval. In order to be approved, dewatering plans must include a plan view indicating the rate, location, and method of dewatering as well as the discharge location and direction of downstream flow, and demonstrating that all dewatering work and discharges will not cause flooding or impoundment, downstream siltation, erosion, or turbid discharges that violate state water quality standards. Plans shall be submitted to: Northwest Florida Water Management District, Environmental Resource Permitting, 700 US Highway 331 S, Defuniak Springs, FL 32435.

(g) The approved facility and lands owned or controlled by the Permittee shall be used as described and identified in the application. If the facility or those lands become part of a subdivision, development, or are used for purposes other than those identified in the application, the facility shall be dewatered until the required permits are obtained and the facility is properly modified or reconstructed.

(h) The District’s staff, upon proper identification, shall be permitted to enter the land where the permitted facilities are located to inspect and observe the facilities in order to determine compliance with the approved plans, specifications and conditions of the permit.

(3) Permits issued by the District shall be subject to other reasonable conditions as are necessary to assure that the project will not be inconsistent with the overall objectives of the District and will not be harmful to the water resources of the District.

Rulemaking Authority 373.044, 373.113, 373.418 FS. Law Implemented 373.413, 373.416, 373.418, 373.419, 373.423, 373.426, 403.927 FS. History–New 10-1-84, Amended 8-1-89, 7-1-92, 3-27-19.

## 40A-44.411 Completion Report.

Within 30 days after the completion of construction or alteration of any project for which a permit was granted under this chapter, the permittee shall file with the District a completion report prepared and certified in accordance with the certification requirements of subsection 40A-44.301(7), F.A.C.

(1) The “As-Built Certification and Completion Report” Form Nos. A44-B or A44-C amended 7-1-92, which are hereby incorporated by reference, shall identify the permit number and shall certify that the project was completed according to the specifications and standards identified in the application and all conditions stipulated by the District. Copies can be obtained by contacting the District, or online at http://www.flrules.org/Gateway/Reference.asp?No=Ref-02965 or http://www.flrules.org/Gateway/Reference.asp?No=Ref-02966, or at the District’s website www.nwfwater.com. Any minor deviations not subject to the requirements of Rule 40A-44.331, F.A.C., for the permitted facility shall be identified in the report and shall be accompanied by supporting engineering documentation.

(2) The project shall not be determined fully complete and shall not be used to impound or convey water until the required “As-Built Certification and Completion Report,” Form Nos. A44-B and A44-C, is submitted to, and verified by a final inspection by, the District.

Rulemaking Authority 373.044, 373.113, 373.418, 403.0877 FS. Law Implemented 373.117, 373.419, 373.423, 403.0877(4) FS. History–New 10-1-84, Amended 8-1-89, 7-1-92, 8-6-13.

## 40A-44.451 Emergency Authorization.

(1) The Executive Director shall grant emergency authorization in accordance with Sections 373.439 and 120.542, F.S. The emergency authorization shall be presented to the Board for concurrence at its next meeting. The failure to receive the Board’s concurrence shall invalidate the emergency authorization.

(2) For projects with pending applications, permission to begin construction of works prior to the issuance of a permit may be applied for to the Governing Board, in writing, when emergency conditions justify. A serious set of unforeseen or unforeseeable circumstances must exist to create an emergency.

Rulemaking Authority 373.044, 373.113, 373.418 FS. Law Implemented 373.439 FS. History–New 10-1-84, Amended 8-6-13.

## 40A-44.461 Inspections.

Rulemaking Authority 373.044, 373.171 FS. Law Implemented 373.423 FS. History–New 10-1-84, Repealed 7-1-98.

## 40A-44.901 Forms.

All District forms are available at the following District office:

DeFuniak Springs Service Office, 700 US Highway 331 S, DeFuniak Springs, FL 32435.

Rulemaking Authority 373.044, 373.113, 373.118, 373.418, 373.4136 FS. Law Implemented 373.116, 373.413, 373.416, 373.426, 373.418 FS. History–New 10-1-84, Amended 7-1-92, 8-6-13.