# CHAPTER 40B-8

# MINIMUM FLOWS AND LEVELS

# 40B-8.011	Policy and Purpose

# 40B-8.021	Definitions

# 40B-8.031	Minimum Surfacewater Levels and Flows

# 40B-8.041	Minimum Surfacewater Levels and Flows for Lower Suwannee River, Little Fanning Spring, Fanning Spring and Manatee Spring

# 40B-8.051	Minimum Surfacewater Levels and Flows for the Waccasassa River and Levy Blue Spring

# 40B-8.061	Minimum Surfacewater Levels and Flows for the Upper Santa Fe River

# 40B-8.071	Minimum Surface Water Levels and Flows for the Econfina River

# 40B-8.081	Minimum Surface Water Levels and Flows for the Aucilla River and Nutall Rise

# 40B-8.091	Minimum Surface Water Levels and Flows for the Wacissa River and Wacissa River Priority Springs

# 40B-8.101	Minimum Flows and Minimum Water Levels for the Steinhatchee River and Steinhatchee River Priority Springs

# 40B-8.121	Minimum Surface Water Levels for Lakes

## 40B-8.011 Policy and Purpose.

(1) This chapter establishes minimum flows and levels for surface waters and minimum levels for groundwater at specific locations within the Suwannee River Water Management District.

(2) Where appropriate, minimum flows and levels may reflect seasonal and long-term variations and may include a schedule of variations and other measures appropriate for the protection of non-consumptive uses of a water resource.

(3) In establishing minimum flows and levels, the Governing Board shall use the best information available to establish limits which prevent significant harm to the water resources or ecology. The Governing Board will also consider and, at its discretion, provide for the protection of non-consumptive uses, including navigation, recreation, fish and wildlife habitat, and other natural resources.

(4) Minimum flows and levels prescribed in this chapter are used as a basis for imposing limitations on withdrawals of groundwater and surface water, for reviewing proposed surfacewater management and storage systems and stormwater management systems, and for imposing water shortage restrictions. The limitations and review criteria which relate to these minimum flows and levels are prescribed in other rule chapters of the District.

Rulemaking Authority 373.044, 373.113, 373.171 FS. Law Implemented 373.042, 373.0421 FS. History–New 9-15-05.

## 40B-8.021 Definitions.

Unless the context indicates otherwise, the following terms shall have the following meanings:

(1) “Aucilla River” means the riverine waterbody that originates in south-central Georgia and flows south and southwest into Florida discharging into the Gulf of Mexico at the border of Jefferson and Taylor Counties, Florida.

(2) “Aucilla River At Lamont, FL gage” means stream flow measuring gage number 02326500 located on the Aucilla River at the border of Taylor and Jefferson Counties, Florida.

(3) “Big Blue Spring” means the spring located within Jefferson County, adjacent to the Wacissa River at 30 degrees 19 minutes 40 seconds north latitude and 83 degrees 59 minutes 5 seconds west longitude.

(4) “Buzzard Log Spring” means the spring located within Jefferson County, adjacent to the Wacissa River at 30 degrees 19 minutes 48 seconds north latitude and 83 degrees 59 minutes 13 seconds west longitude.

(5) “Cassidy Spring” means the spring located within Jefferson County, adjacent to the Wacissa River at 30 degrees 19 minutes 58 seconds north latitude and 83 degrees 59 minutes 21 seconds west longitude.

(6) “Econfina River” means the riverine waterbody that originates in Taylor County, Florida and flows south and southwest discharging into the Gulf of Mexico in Taylor County, Florida.

(7) “Econfina River Near Perry, FL gage” means stream flow measuring gage number 02326000 located on the Econfina River in Taylor County, Florida.

(8) “Fanning Spring” means the single spring vent located within Levy County, adjacent to the Suwannee River at 29 degrees 33 minutes 14 seconds north latitude and 82 degrees 56 minutes 07 seconds west longitude.

(9) “Flow Duration Curve” means a statistical representation of flows, actual or synthetic, and their recurrence probabilities over a determined period of record.

(10) “Flow duration frequency” means the historic probability of a particular flow over a specified period of record.

(11) “Garner Spring” means the spring located within Jefferson County, adjacent to the Wacissa River at 30 degrees 19 minutes 49 seconds north latitude and 83 degrees 58 minutes 59 seconds west longitude.

(12) “Historic period” means the period of record as documented in each technical report establishing minimum flow or level.

(13) “JEF63991” means the spring located within Jefferson County, adjacent to the Wacissa River at 30 degrees 19 minutes 30 seconds north latitude and 83 degrees 59 minutes 9 degrees west longitude.

(14) “JEF63992” means the spring located within Jefferson County, adjacent to the Wacissa River at 30 degrees 19 minutes 23 seconds north latitude and 83 degrees 59 minutes 12 degrees west longitude.

(15) “JEF63993” means the spring located within Jefferson County, adjacent to the Wacissa River at 30 degrees 18 minutes 8 seconds north latitude and 83 degrees 58 minutes 47 seconds west longitude.

(16) “Jefferson Blue Spring” means the spring located within Jefferson County, adjacent to the Wacissa River at 30 degrees 19 minutes 50 seconds north latitude and 83 degrees 59 minutes 20 seconds west longitude.

(17) “Levy Blue Spring” means the single spring vent located within Levy County, near the Town of Bronson, adjacent to the Waccasassa River at 29 degrees 27 minutes 03 seconds north latitude and 82 degrees 41 minutes 56 seconds west longitude.

(18) “Little Blue Spring” means the spring located within Jefferson County, adjacent to the Wacissa River at 30 degrees 19 minutes 51 seconds north latitude and 83 degrees 59 minutes 21 seconds west longitude.

(19) “Little Fanning Spring” means the single spring vent located within Levy County, adjacent to the Suwannee River at 29 degrees 35 minutes 09 seconds north latitude and 82 degrees 56 minutes 04 seconds west longitude.

(20) “Log Spring” means the spring located within Jefferson County, adjacent to the Wacissa River at 30 degrees 20 minutes 26 seconds north latitude and 83 degrees 59 minutes 35 seconds west longitude.

(21) “Lower Suwannee River” means the river segment below the Wilcox gage to the estuary.

(22) “Madison Blue Spring” means the single vent spring system located within Madison County, adjacent to the Withlacoochee River at 30 degrees 28 minutes 48 seconds north latitude and 83 degrees 14 minutes 40 seconds west longitude.

(23) “Manatee Spring” means the single spring vent located within Levy County, adjacent to the Suwannee River at 29 degrees 29 minutes 21 seconds north latitude and 82 degrees 58 minutes 37 seconds west longitude.

(24) “Minimum surfacewater flow” means a flow, expressed in cubic feet per second combined with a temporal element. The temporal element may be specifically expressed as a duration and return interval.

(25) “Minimum surfacewater level” means an elevation in feet NGVD combined with a temporal element. The temporal element, for purposes of this chapter, may be specifically expressed as a duration and return interval.

(26) “Minnow Spring” means the spring located within Jefferson County, adjacent to the Wacissa River at 30 degrees 19 minutes 54 seconds north latitude and 83 degrees  59 minutes 12 seconds west longitude.

(27) “NAVD” means North American Vertical Datum of 1988.

(28) “NGVD” means National Geodetic Vertical Datum of 1929.

(29) “Nutall Rise” means the spring located on the border of Jefferson and Taylor counties, adjacent to the Aucilla River at 30 degrees 9 minutes 2 seconds north latitude and 83 degrees 57 minutes 48 seconds west longitude.

(30) “Santa Fe River” means the riverine waterbody that originates in Lake Santa Fe, Alachua County, Florida and flows west discharging into the Suwannee River south of Branford, Florida.

(31) “Santa Fe River at Worthington Springs, FL gage” means stream flow measuring gage number 02321500 located on the Santa Fe River 0.8 mile downstream from New River at 29 degrees 55 minutes 18 seconds north latitude and 82 degrees 25 minutes 35 seconds west longitude, in Alachua County.

(32) “Santa Fe River Near Graham, FL gage” means stream flow measuring gage number 02320700 located on the Santa Fe River approximately 1.5 miles upstream from Sampson River at 29 degrees 50 minutes 46 seconds north latitude and 82 degrees 13 minutes 11 seconds west longitude, in Alachua County.

(33) “Stage Duration Frequency” means a statistical representation of stages, actual or synthetic, and their recurrence probabilities over a determined period of record.

(34) “Steinhatchee Rise” means the spring located within Dixie County, adjacent to the Steinhatchee River at 29 degrees 46 minutes 12 seconds north latitude and 83 degrees 19 minutes 30 seconds west longitude.

(35) “Steinhatchee River” means the riverine waterbody, its tributaries and estuary that originate from diffuse runoff and groundwater discharge in Lafayette and Taylor counties, Florida and flows south-southwest, generally forming the boundary between Dixie and Taylor counties, before discharging into the Gulf of Mexico near Steinhatchee, Florida.

(36) “Steinhatchee River Near Cross City, FL gage” means the stream flow measuring gage number 02324000 located on the Steinhatchee River at 29 degrees 47 minutes 11 seconds north latitude and 83 degrees 19 minutes 18 seconds west longitude.

(37) “Suwannee River” means the riverine waterbody that originates in south-central Georgia and flows southeast and south into Florida discharging into the Gulf of Mexico north of Cedar Key, Florida.

(38) “Suwannee River Near Wilcox, FL gage” means stream flow measuring gage number 02323500 located on the Suwannee River at 29 degrees 35 minutes 22 seconds north latitude and 82 degrees 56 minutes 12 seconds west longitude.

(39) “TAY76992” or “Beaver Creek Spring” means the spring located within Taylor County, adjacent to the Steinhatchee River at 29 degrees 45 minutes 41 seconds north latitude and 83 degrees 20 minutes 06 seconds west longitude.

(40) “Thomas Spring” means the spring located within Jefferson County, adjacent to the Wacissa River at 30 degrees 20 minutes 23 seconds north latitude and 83 degrees 59 minutes 32 seconds west longitude.

(41) “Waccasassa River and Estuary” means the riverine waterbody that originates in Gilchrist and Alachua counties and flows southwest discharging into the Gulf of Mexico between Cedar Key and Yankeetown, Florida.

(42) “Waccasassa River Near Gulf Hammock, FL gage” means stream flow measuring gage number 02313700 located on the Waccasassa River 0.5 mile upstream from Otter Creek at 29 degrees 12 minutes 14 seconds north latitude, 82 degrees 46 minutes 09 seconds west longitude in Levy County.

(43) “Wacissa Head Spring” means the spring located within Jefferson County, adjacent to the Wacissa River at 30 degrees 20 minutes 24 seconds north latitude and 83 degrees 59 minutes 29 seconds west longitude.

(44) “Wacissa River” means the riverine waterbody that originates from a spring system in Jefferson County, Florida and flows southeast diffusing into numerous braids before discharging into the Aucilla River.

(45) “Wacissa River Near Wacissa, FL gage” means stream flow measuring gage number 02326526 located on the Wacissa River in Jefferson County, Florida.

(46) “Withlacoochee River” means the riverine waterbody that originates in south-central Georgia and flows southeast and south into Florida discharging into the Suwannee River at Ellaville, Florida.

(47) “Withlacoochee River Near Pinetta, FL gage” means stream flow measuring gauge number 02319000 located on the Withlacoochee River approximately 10 miles upstream from Madison Blue Spring at 30 degrees 35 minutes 43 seconds north latitude and 83 degrees 15 minutes 35 seconds west longitude.

Rulemaking Authority 373.044, 373.113 FS. Law Implemented 373.042 FS. History–New 9-15-05, Amended 8-7-06, 7-29-07, 12-10-07, 6-27-16, 8-15-19, 8-9-21.

## 40B-8.031 Minimum Surfacewater Levels and Flows for Madison Blue Spring.

The Governing Board hereby establishes the following minimum surfacewater flows and levels for Madison Blue Spring. The Governing Board finds that the following minimum surfacewater flows and levels are the limit at which further withdrawals would be significantly harmful to the water resources or ecology.

(1) The minimum surfacewater flow for Madison Blue Spring is 70 cubic feet per second (cfs) for a flow duration frequency of 90 percent when the stage of the Withlacoochee River measured at the Pinetta gauge is 55.0 feet (NGVD) or less.

(2) If the surfacewater flows from Madison Blue Spring are reduced below the levels established in subsection (1) above, withdrawals will be significantly harmful to the water resources or ecology.

(3) In determining the estimated impact of existing and proposed future withdrawals on the surfacewater flow of Madison Blue Spring, as expressed in subsections (1) and (2) above, the following factors shall be considered:

(a) A stage of 55.0 feet (NGVD) at the Pinetta gauge will serve as a modeling boundary condition.

(b) The surfacewater flow for Madison Blue Spring shall not be caused to be reduced to a predicted flow of 70 cfs or less for a flow duration frequency of less than 90 percent as determined by the Flow Duration Curve for the Madison Blue Spring discharge over the historic period.

Rulemaking Authority 373.044, 373.113 FS. Law Implemented 373.042, 373.0421, 373.103, 373.415 FS. History–New 9-15-05, Amended 8-7-06.

## 40B-8.041 Minimum Surfacewater Levels and Flows for Lower Suwannee River, Little Fanning Spring, Fanning Spring, and Manatee Spring.

The Governing Board hereby establishes the following minimum surfacewater flows and levels. The Governing Board finds that the following minimum surfacewater flows and levels are the limit at which further withdrawals would be significantly harmful to the water resources or ecology.

(1) The minimum surfacewater flow for Manatee Spring is the flow that will maintain 90 percent of the historic flow regime for the Manatee Spring discharge as defined in “Technical Report – MFL Establishment for the Lower Suwannee River and Estuary, Little Fanning, Fanning, and Manatee Springs, October 2005.”

(2) In addition to subsection (1) above, the minimum surface water flow for Manatee Spring for the period of November 1 through April 30 is 130 cubic feet per second for a flow duration frequency of 50 percent.

(3) The minimum surfacewater flow for Fanning and Little Fanning Spring is the flow that will maintain 90 percent of the historic flow regime for the Fanning Spring discharge as defined in “Technical Report – MFL Establishment for the Lower Suwannee River and Estuary, Little Fanning, Fanning, and Manatee Springs, October 2005.”

(4) The minimum surface water level for Fanning Spring for the period of November 1 through April 30 is 2.71 feet (NGVD) for a stage duration frequency of 85 percent.

(5) The minimum surfacewater flow for the Lower Suwannee River below the Wilcox gauge is 6,600 cubic feet per second for a flow duration frequency of 50 percent for the period May 1 through October 31. For the period November 1 through April 30, the minimum surfacewater flow is 7,600 cubic feet per second for a flow duration frequency of 50 percent.

Rulemaking Authority 373.044, 373.113 FS. Law Implemented 373.042, 373.0421, 373.103, 373.415 FS. History–New 8-7-06.

## 40B-8.051 Minimum Surface Water Levels and Flows for Waccasassa River and Estuary and Levy Blue Spring.

The Governing Board hereby establishes the following minimum surfacewater flows. The Governing Board finds that the following minimum surfacewater flows are the limit at which further withdrawals would be significantly harmful to the water resources or ecology.

(1) The minimum surfacewater flow for Levy Blue Spring is the flow that will maintain 90 percent of the historic flow regime for the Levy Blue Spring discharge as defined in “Technical Report-MFL Establishment for the Waccasassa River, Estuary and Levy (Bronson) Blue Spring, June 2006.”

(2) The minimum surfacewater flow for Waccasassa River and Estuary is the flow that will maintain 87.5 percent of the historic flow regime for the Waccasassa River discharge as measured at the United States Geological Survey Gulf Hammock gauge and further defined in “Technical Report- MFL Establishment for the Waccasassa River and Estuary and Levy (Bronson) Blue Spring, June 2006.”

Rulemaking Authority 373.044, 373.113 F.S. Law Implemented 373.042, 373.0421, 373.103, 373.415 FS. History–New 7-29-07.

## 40B-8.061 Minimum Surface Water Levels and Flows for the Santa Fe River.

The Governing Board hereby establishes the following minimum surfacewater flows. The Governing Board finds that the following minimum surfacewater flows are the limit at which further withdrawals would be significantly harmful to the water resources or ecology.

(1) The minimum surfacewater flows for the Santa Fe River Near Graham, FL, gage are the following points on the flow duration curve defined in “Technical Report – MFL Establishment for the Upper Santa Fe River, May 2007”:

(a) 171 cubic feet per second (cfs) for a flow duration frequency of five percent;

(b) 109 cfs for a flow duration frequency of 10 percent;

(c) 44 cfs for a flow duration frequency of 25 percent;

(d) 13 cfs for a flow duration frequency of 50 percent;

(e) 2.3 cfs for a flow duration frequency of 75 percent;

(f) 0.4 cfs for a flow duration frequency of 90 percent;

(g) 0.2 cfs for a flow duration frequency of 95 percent.

(2) The minimum surfacewater flows for the Santa Fe River at Worthington Springs, FL, gage are the following points on the flow duration curve defined in “Technical Report – MFL Establishment for the Upper Santa Fe River, May 2007”:

(a) 1,513 cfs for a flow duration frequency of five percent;

(b) 935 cfs for a flow duration frequency of 10 percent;

(c) 367 cfs for a flow duration frequency of 25 percent;

(d) 111 cfs for a flow duration frequency of 50 percent;

(e) 42 cfs for a flow duration frequency of 75 percent;

(f) 15 cfs for a flow duration frequency of 90 percent;

(g) 9 cfs for a flow duration frequency of 95 percent.

Rulemaking Authority 373.044, 373.113 FS. Law Implemented 373.042, 373.0421, 373.103 FS. History–New 12-10-07.

40B-8.071 Minimum Surface Water Levels and Flows for the Econfina River.

The Governing Board hereby establishes the following minimum surfacewater flows. The Governing Board finds that the following minimum surfacewater flows are the limit at which further withdrawals would be significantly harmful to the water resources or ecology.

The minimum surfacewater flow for the Econfina River Near Perry, FL gage is an allowable reduction of 23 percent when flow is below 211 cubic feet per second (cfs) and 8.6 percent when flow is greater than or equal 211 cfs.

Rulemaking Authority 373.044, 373.113 FS. Law Implemented 373.042, 373.0421, 373.103 FS. History–New 5-24-16.

40B-8.081 Minimum Surface Water Levels and Flows for the Aucilla River and Nutall Rise.

The Governing Board hereby establishes the following minimum surfacewater flows. The Governing Board finds that the following minimum surfacewater flows are the limit at which further withdrawals would be significantly harmful to the water resources or ecology.

(1) The minimum surfacewater flow for the Aucilla River At Lamont, FL gage is an allowable reduction of 6.5 percent when flow is less than or equal to 355 cubic feet per second (cfs), 13 percent when flow is greater than 355 cfs and is less than or equal to 558 cfs, and 17 percent when flow is greater than 558 cfs.

(2) The minimum surface water flow for Nutall Rise is established as a percent reduction from the median flow contribution to the Aucilla River. The allowable reduction in flow of Nutall Rise is 6.5 percent from the median flow.

Rulemaking Authority 373.044, 373.113 FS. Law Implemented 373.042, 373.0421, 373.103 FS. History–New 5-24-16.

40B-8.091 Minimum Surface Water Levels and Flows for the Wacissa River and Wacissa River Priority Springs.

The Governing Board hereby establishes the following minimum surfacewater flows. The Governing Board finds that the following minimum surfacewater flows are the limit at which further withdrawals would be significantly harmful to the water resources or ecology.

(1) The minimum surfacewater flow for the Wacissa River Near Wacissa, FL gage is an allowable reduction in flow of 5.1 percent when flow is less than or equal to 376 cubic feet per second (cfs) and 7.3 percent when flow is greater than or equal to 376 cfs.

(2) The minimum surface water flows for the Wacissa River Priority Springs are established as the following percent reductions from the median flow contribution to the Wacissa River:

(a) Big Blue Spring: 6.5 percent;

(b) Buzzard Log Spring: 6.5 percent;

(c) Cassidy Spring: 6.5 percent;

(d) Garner Spring: 6.5 percent;

(e) JEF63991: 6.5 percent;

(f) JEF63992: 6.5 percent;

(g) JEF63993: 6.5 percent;

(h) Jefferson Blue Spring: 6.5 percent;

(i) Little Blue Spring: 6.5 percent;

(j) Log Spring: 6.5 percent;

(k) Minnow Spring: 6.5 percent;

(l) Thomas Spring: 6.5 percent;

(m) Wacissa Headspring: 6.5 percent.

Rulemaking Authority 373.044, 373.113 FS. Law Implemented 373.042, 373.0421, 373.103 FS. History–New 5-24-16.

## 40B-8.101 Minimum Flows and Minimum Water Levels for the Steinhatchee River and Steinhatchee River Priority Springs.

The Governing Board hereby establishes the following minimum flows. The Governing Board finds that the following minimum flows are the limit at which further withdrawals would be significantly harmful to the water resources or ecology.

(1) The minimum surface water flow for the Steinhatchee River occurs when the cumulative change in flow at the Steinhatchee River Near Cross City, FL gage is greater than 2.07 cubic feet per second (cfs) from a flow that has been unchanged by groundwater withdrawals, surface water withdrawals, or a combination of both.

(2) The minimum surface water flows for the Steinhatchee River priority springs are established as the following cumulative percent reductions from the median flow of such springs measured at the spring vent or as close thereto as reasonably possible:

(a) TAY76992: 11.5 percent;

(b) Steinhatchee Rise: 11.5 percent.

(3) In addition to the criterion set forth in subsection 40B-8.101(1), F.A.C., a cumulative surface water flow reduction of 11.5 percent of the prior day’s flow at the Steinhatchee River Near Cross City, FL gage when flow is greater than 8.70 cfs and less than or equal to 858 cfs, or a cumulative reduction in flow of 98.7 cfs when flow is greater than 858 cfs and less than or equal to 1,790 cfs, or a cumulative reduction in flow of 5.5 percent when flow is greater than 1,790 cfs does not result in significant harm. For the purposes of this section, the “prior day’s average flow” will be the daily mean discharge in cfs for the previous calendar day measured at the Steinhatchee River Near Cross City, FL gage.

Rulemaking Authority 373.044, 373.113 FS. Law Implemented 373.042, 373.0421, 373.103 FS. History–New 8-15-19.

## 40B-8.121 Minimum Surface Water Levels for Lakes.

(1) The following terms, as used in this rule, shall have the following meanings:

(a) “High Minimum Lake Level” means the surface water level the lake must meet or exceed ten percent of the time on a long-term basis to ensure it reaches higher levels on a periodic basis.

(b) “Minimum Average” means the surface water level or flow necessary over a long period to maintain the integrity of hydric soils and wetland plant communities.

(c) “Minimum Frequent High” means a chronically high surface water level or flow with an associated frequency and duration that allows for inundation of the floodplain at a depth and duration sufficient to maintain wetland functions.

(d) “Minimum Frequent Low” means a chronically low surface water level or flow that generally occurs only during periods of reduced rainfall. This level is intended to prevent deleterious effects to the composition and structure of floodplain soils, the species composition and structure of floodplain and instream biotic communities, and the linkage of aquatic and floodplain food webs.

(e) “Minimum Lake Level” means the surface water level the lake must meet or exceed fifty percent of the time on a long-term basis to maintain average conditions.

(f) “Seasonally Flooded” means a hydroperiod category where surface water is typically present for extended periods (30 days or more) during the growing season, resulting in a predominance of submerged or submerged and transitional wetland species. During extended periods of normal or above normal rainfall, lake levels causing inundation are expected to occur several weeks to several months every one to two years.

(g) “Semi-Permanently Flooded” means a hydroperiod category where surface water inundation persists in most years. When surface water is absent the water table is usually near the land surface. In many lakes with emergent marshes this water level is near the lower elevation that supports emergent marsh or floating vegetation and peat substrates, or other highly organic hydric substrates. This characterization may not be true for herbaceous wetlands around sandhill type lakes, which often have emergent vegetation that follows declining water levels to below the lower elevation of peat substrate. Water levels causing inundation are expected to occur approximately eighty percent of the time over a long-term period of record. Exposure of these ground elevations is expected to re-occur, on average, about every five to ten years for extended periods (several or more months) during moderate droughts.

(h) “Typically Saturated” means a hydroperiod category where, for extended periods of the year, the water level should saturate or inundate. This condition results in saturated substrates for periods of one-half year or more during non-flooding periods of typical years. Water levels causing inundation are expected to occur fifty to sixty per cent of the time over a long-term period of record. This water level is expected to have a recurrence interval, on the average, of one or two years over a long-term period of record. Obligate wetland plant species are expected to be predominate near this water level.

(2) The following minimum surface water levels are established:

| Water Body Name | County (Latitude/ Longitude) | Minimum Level | Level (Feet NAVD) | Event | Hydroperiod Category | Duration (Days) | Return Interval (Interval Measurement Period) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Lake Butler | Union (30º02ꞌ00ꞌꞌN/ 082º20ꞌ12ꞌꞌW) | Minimum Frequent High | 129.55 | Flooding | Seasonally flooded | 30 | 2 years (June 1 to May 31) |
|  |  | Minimum Frequent Low | 127.30 | Exposure | Semi-permanently flooded | 120 | 5 years (October 1 to September 30) |
| Lake Hampton | Bradford (29º51ꞌ42ꞌꞌN/ 082º10ꞌ10ꞌꞌW) | High Minimum Lake Level | 128.86 |  |  |  |  |
|  |  | Minimum Lake Level | 128.15 |  |  |  |  |
| Lake Santa Fe | Alachua (29o44ꞌ45ꞌꞌN/082o04ꞌ45ꞌꞌW) | Minimum Frequent High | 139.10 | Flooding | Seasonally flooded | 30 | 2 years (June 1 to May 31) |
|  |  | Minimum Average | 137.89 | Exposure | Typically saturated | 180 | 1.7 years (October 1 to September 30) |
|  |  | Minimum Frequent Low | 136.52 | Exposure | Semi-permanently flooded | 120 | 5 years (October 1 to September 30) |

Rulemaking Authority 373.044, 373.113 FS. Law Implemented 373.042, 373.0421, 373.103 FS. History–New 8-9-21, Amended 3-12-23.