# CHAPTER 5J-21

# MOTOR FUEL SPECIFICATIONS AND STANDARDS

# 5J-21.001	Standards

# 5J-21.002	Disposition of Below Standard Gasoline, Kerosene, Diesel Fuel Oils No. 1-D and No. 2-D, and Fuel Oils No. 1 	and No. 2, and Alternative Fuels

# 5J-21.003	Registration and Identification

# 5J-21.004	Motor Fuel Price Posting

# 5J-21.005	Inaccurate Measuring Devices

# 5J-21.006	Inspection Identification Stickers

# 5J-21.007	Adoption of the General Code and the Codes of Liquid-Measuring Devices, Liquefied Petroleum Gas and Anhydrous Ammonia Liquid-Measuring Devices, Hydrocarbon Gas Vapor-Measuring Devices, Vehicle-Tank Meters, Vehicle Tanks Used as Measures of National Institute of Standards and Technology Handbook 44 Meter Sealing Requirements, and Other Related Requirements

# 5J-21.008	Guidelines for Imposing Administrative Penalties

# 5J-21.009	Security Measures for Petroleum Fuel Measuring Devices

## 5J-21.001 Standards.

(1) Gasoline (includes gasoline blended with oxygenates). The following specifications apply to gasoline sold or offered for sale in Florida. Specific variations or exemptions shall be considered by the Department of Agriculture and Consumer Services for gasoline designed for special equipment or service in accordance with Section 120.542, F.S., Variances and Waivers.

(a) Standards. All gasoline shall conform to the chemical and physical standards for gasoline as set forth in ASTM International Designation D4814-20a (approved April 1, 2020), “Standard Specification for Automotive Spark-Ignition Engine Fuel”, with the following exceptions, providing that the base gasoline used under the exceptions conforms to the chemical and physical standards for gasoline as set forth in ASTM International Designation D4814-20a (approved April 1, 2020), “Standard Specification for Automotive Spark-Ignition Engine Fuel” except where noted:

1. Vapor Pressure Class Requirements: Gasoline containing at least one (1) percent ethanol by volume shall be allowed a 1.0 psi increase to the applicable vapor pressure class maximum from September 16 through May 31 (not applicable for gasoline/ethanol blend tankage at refineries, importers, pipelines, and terminals for the month of May). From June 1 (May 1 for gasoline/ethanol blend tankage at refineries, importers, pipelines, and terminals) through September 15, gasoline blends containing ethanol shall conform to the vapor pressure class requirements and are entitled to the permissible increases provided by the Environmental Protection Agency (EPA) and outlined in ASTM International Designation D4814-20a (approved April 1, 2020), “Standard Specification for Automotive Spark-Ignition Engine Fuel.”

2. If, prior to blending with ethanol, the base gasoline has either a maximum distillation temperature at the fifty volume percent evaporated distillation point of up to 10° F above the maximum or has a driveability index (DI) of up to 30 above the maximum, as stated for the proper distillation class in ASTM International Designation D4814-20a (approved April 1, 2020), “Standard Specification for Automotive Spark-Ignition Engine Fuel”, or has both, the fuel may be sold, distributed or offered for sale or distribution provided that the department is contacted at (850)921-1545 prior to exercising this option and is provided with a documented company statement attesting to and demonstrating the following:

a. The affected fuel will only be sold, offered for sale, distributed or offered for distribution after blending with at least nine (9%) percent ethanol, by volume.

b. The base gasoline meets all other specifications for spark-ignition engine fuels as set forth in ASTM International Designation D4814-20a (approved April 1, 2020), “Standard Specification for Automotive Spark-Ignition Engine Fuel.”

c. The fuel meets all specifications for gasoline as defined in this subsection after blending with at least nine (9%) percent ethanol, by volume.

d. The fuel will be tested by the owner after blending (hand blend samples are acceptable), but before selling, distributing, offering for sale or distribution, and it shall be demonstrated that the fuel meets all specifications for gasoline as defined in ASTM International Designation D4814-20a (approved April 1, 2020), “Standard Specification for Automotive Spark-Ignition Engine Fuel”, which shall be displayed on a certificate of analysis or laboratory report. Such documentation must be made available to the department upon request.

e. The storage location(s) of the fuel intended to be blended under this provision.

(b) Analysis. For purposes of inspection and testing, laboratory analyses shall be conducted using the methods recognized by ASTM International Designation D4814-20a (approved April 1, 2020), “Standard Specification for Automotive Spark-Ignition Engine Fuel.”

(c) No person shall sell or offer for sale gasoline in this state that does not comply with the following requirements:

1. The total ethanol content of gasoline shall not exceed fifteen percent (15%), by volume; or

2. The total methanol with co-solvents content of gasoline shall not exceed seven and one half percent (7.5%), where methanol does not exceed five percent (5%) and the co-solvents do not exceed two and one half percent (2.5%), by volume; or

3. The total methyl tertiary butyl ether (MTBE) content of gasoline shall not exceed two percent (2%), by volume; or

4. The total ethanol and methyl tertiary butyl ether (MTBE) content of gasoline shall not exceed fifteen percent (15%), by volume; or

5. The total butanol content of gasoline shall not exceed twelve and one half percent (12.5%), by volume.

(d) All gasoline sold or distributed at retail, or offered for sale or distribution at retail shall have an octane rating ((R+M)/2) of at least 87.

(e) All gasoline with an octane rating ((R+M)/2) of 87 or higher shall have a motor octane number (MON) of at least 82.

(2) Kerosene (Kerosine). The following specifications apply to kerosene No. 1-K and No. 2-K sold or offered for sale in Florida.

(a) Standards. All kerosene No. 1-K and No. 2-K shall conform to the chemical and physical standards for kerosene No. 1-K and No. 2-K as set forth in ASTM International Designation D3699-19 (approved December 15, 2019), “Standard Specification for Kerosine.”

(b) Analysis. For purposes of inspection and testing, laboratory analyses shall be conducted using the methods recognized by ASTM International Designation D3699-19 (approved December 15, 2019), “Standard Specification for Kerosine.”

(3) Diesel Fuels No. 1-D and No. 2-D. The following specifications apply to diesel fuels No. 1-D and No. 2-D sold or offered for sale in Florida.

(a) Standards. All diesel fuels No. 1-D and No. 2-D shall conform to the chemical and physical standards for diesel fuels No. 1-D and No. 2-D as set forth in ASTM International Designation D975-20a (approved June 1, 2020), “Standard Specification for Diesel Fuel.”

(b) Analysis. For purposes of inspection and testing, laboratory analyses shall be conducted using the methods recognized by ASTM International Designation D975-20a (approved June 1, 2020), “Standard Specification for Diesel Fuel.”

(4) Fuel Oils No. 1 and No. 2. The following specifications apply to fuel oils No. 1 and No. 2 sold or offered for sale in Florida.

(a) Standards. All fuel oils No. 1 and No. 2 shall conform to the chemical and physical standards for fuel oils No. 1 and No. 2 as set forth in ASTM International Designation D396-20 (approved June 1, 2020), “Standard Specification for Fuel Oils.”

(b) Analysis. For purposes of inspection and testing, laboratory analyses shall be conducted using the methods recognized by ASTM International Designation D396-20 (approved June 1, 2020), “Standard Specification for Fuel Oils.”

(5) Alternative Fuels.

(a) Denatured Ethanol.

1. Standards. All denatured fuel ethanol shall conform to the chemical and physical standards for denatured fuel ethanol as set forth in the ASTM International Designation D4806-20 (approved May 1, 2020), “Standard Specification for Denatured Fuel Ethanol for Blending with Gasolines for Use as Automotive Spark-Ignition Engine Fuel.”

2. Analysis. For purposes of inspection and testing, laboratory analyses shall be conducted using the methods recognized by the ASTM International Designation D4806-20 (approved May 1, 2020), “Standard Specification for Denatured Fuel Ethanol for Blending with Gasolines for Use as Automotive Spark-Ignition Engine Fuel.”

(b) Methanol Fuel Blends (51 to 85 volume percent methanol). The following specifications apply to Methanol Fuel Blends (51 to 85 volume percent methanol) sold or offered for sale in Florida.

1. Standards. All Methanol Fuel Blends (51 to 85 volume percent methanol) shall conform to the chemical and physical standards for Methanol Fuel Blends (51 to 85 Volume percent methanol) as set forth in the ASTM International Designation D5797-18 (approved December 1, 2018), “Standard Specification for Methanol Fuel Blends (M51-M85) for Methanol-Capable Automotive Spark-Ignition Engines” and shall conform to the end-point distillation temperature requirements for gasoline, as defined in subsection 5J-21.001(1), F.A.C.

2. Analysis. For purposes of inspection and testing, laboratory analyses shall be conducted using the methods recognized by the ASTM International Designation D5797-18 (approved December 1, 2019), “Standard Specification for Methanol Fuel Blends (M51-M85) for Methanol-Capable Automotive Spark-Ignition Engines.”

(c) Mixtures of Denatured Ethanol.

1. Ethanol Fuel Blends (51 to 83 volume percent ethanol). The following specifications apply to Ethanol Fuel Blends (51 to 83 volume percent ethanol) sold or offered for sale in Florida.

a. Standards. All Ethanol Fuel Blends (51 to 83 volume percent ethanol) shall conform to the chemical and physical standards for Ethanol Fuel Blends (51 to 83 volume percent ethanol) as set forth in the ASTM International Designation D5798-20 (approved May 1, 2020), “Standard Specification for Ethanol Fuel Blends for Flexible-Fuel Automotive Spark-Ignition Engines” and shall conform to the end-point distillation temperature requirements for gasoline, as defined in subsection 5J-21.001(1), F.A.C.

b. Analysis. For purposes of inspection and testing, laboratory analyses shall be conducted using the methods recognized by the ASTM International Designation D5798-20 (approved May 1, 2020), “Standard Specification for Ethanol Fuel Blends for Flexible-Fuel Automotive Spark-Ignition Engines.”

2. Mid-Level Ethanol Blends. The following specifications shall apply to automotive spark-ignition engine fuels with ethanol concentrations greater than that which is permitted in subsection 5J-21.001(1), F.A.C., and less than that which is permitted in subparagraph 5J-21.001(5)(c)1., F.A.C., sold or offered for sale in Florida.

a. Standards. All mid-level ethanol blends shall conform to the practices as set forth in the ASTM International Designation D7794-20 (approved July 1, 2020), “Standard Practice for Blending Mid-Level Ethanol Fuel Blends for Flexible-Fuel Vehicles with Automotive Spark-Ignition Engines” and shall conform to the end-point distillation temperature requirements for gasoline, as defined in subsection 5J-21.001(1), F.A.C.

b. Analysis. For purposes of inspection and testing, laboratory analyses shall be conducted using the methods recognized by the ASTM International Designation D7794-20 (approved July 1, 2020), “Standard Practice for Blending Mid-Level Ethanol Fuel Blends for Flexible-Fuel Vehicles with Automotive Spark-Ignition Engines.”

(d) Fuels, other than alcohol, derived from biological materials:

1. Biodiesel fuel blend stock (also referred to as biodiesel or B100) and B99 (99% biodiesel and 1% diesel fuel by volume). The following specifications apply to biodiesel and B99 sold or offered for sale in Florida.

a. Standards. Biodiesel and B99 shall meet the specifications set forth by ASTM International Designation D6751-20 (approved January 1, 2020), “Standard Specification for Biodiesel Fuel Blend Stock (B100) for Middle Distillate Fuels.”

b. Analysis. For purposes of inspection and testing, laboratory analyses shall be conducted using the methods recognized by the ASTM International Designation D6751-20 (approved January 1, 2020), “Standard Specification for Biodiesel Fuel Blend Stock (B100) for Middle Distillate Fuels.”

2. Biodiesel blends (biodiesel blended with diesel fuel or fuel oil). The following specifications apply to biodiesel blends sold or offered for sale in Florida. Biodiesel blends cannot contain more than 20% biodiesel. B99 is not considered a blend for the purposes of this subparagraph.

a. Standards. Biodiesel blends containing diesel fuel and 6% or more biodiesel shall meet the specifications set forth by ASTM International Designation D7467-20a (approved June 1, 2020), “Standard Specification for Diesel Fuel Oil, Biodiesel Blend (B6 to B20).”

b. Standards. Biodiesel blends containing diesel fuel and less than 6% biodiesel shall meet the specifications set forth by ASTM International Designation D975-20a (approved June 1, 2020), “Standard Specification for Diesel Fuel.”

c. Standards. Biodiesel blends containing fuel oil shall meet the specifications set forth by ASTM International Designation D396-20 (approved June 1, 2020), “Standard Specification for Fuel Oils.”

d. Analysis. For purposes of inspection and testing biodiesel blends containing diesel fuel and 6% or more biodiesel, laboratory analyses shall be conducted using the methods recognized by the ASTM International Designation D7467-20a (approved June 1, 2020), “Standard Specification for Diesel Fuel Oil, Biodiesel Blend (B6 to B20).”

e. Analysis. For purposes of inspection and testing biodiesel blends containing diesel fuel and less than 6% biodiesel, laboratory analyses shall be conducted using the methods recognized by ASTM International Designation D975-20a (approved June 1, 2020), “Standard Specification for Diesel Fuel.”

f. Analysis. For purposes of inspection and testing biodiesel blends containing fuel oil, laboratory analyses shall be conducted using the methods recognized by the ASTM International Designation D396-20 (approved June 1, 2020), “Standard Specification for Fuel Oils.”

(e) Butanol.

1. Standards. All butanol shall conform to the chemical and physical standards for butanol as set forth in the ASTM International Designation D7862-19 (approved May 1, 2020), “Standard Specification for Butanol for Blending with Gasoline for Use as Automotive Spark-Ignition Engine Fuel.”

2. Analysis. For purposes of inspection and testing, laboratory analyses shall be conducted using the methods recognized by the ASTM International Designation D7862-19 (approved May 1, 2019), “Standard Specification for Butanol for Blending with Gasoline for Use as Automotive Spark-Ignition Engine Fuel.”

(6) Water in Retail Storage Tanks.

(a) Water in retail storage tanks containing petroleum fuels, with the exception of products listed in paragraph (6)(b), enumerated in this rule shall not exceed one inches in depth when measured from the bottom of the tank.

(b) Water in retail storage tanks containing gasoline blended with 1% or more ethanol, by volume; Ethanol Fuel Blends; Methanol Fuel Blends; biodiesel; or biodiesel blends containing 1% or more biodiesel, by volume, shall not exceed one quarter inch in depth when measured from the bottom of the tank.

(7) Compressed Natural Gas (CNG) and Liquefied Natural Gas (LNG) Standards.

(a) The general codes for CNG and LNG as enumerated in the National Institute of Standards and Technology (NIST) Handbook 44, as incorporated by reference in Rule 5J-22.002, F.A.C.

(b) The Uniform Regulation for the Method of Sale of Commodities for CNG and LNG as enumerated in the National Institute of Standards and Technology (NIST) Handbook 130, as incorporated by reference in Rule 5J-22.003, F.A.C.

(8) In accordance with Section 525.035, F.S., any petroleum fuel that fails to meet applicable labeling requirements, as adopted in this rule chapter, shall be placed under Stop Sale Order by the department. The measuring devices of said product shall be sealed by the department prohibiting the sale of the petroleum fuel. The petroleum fuel shall be released by the department from the Stop Sale Order in accordance with Section 525.035, F.S.

(9) In accordance with Section 525.037, F.S., any petroleum fuel that fails to meet applicable standards, as adopted in this rule chapter, shall be placed under Stop Sale Order by the department, and the measuring devices of said petroleum fuel shall be sealed by the department, prohibiting the sale of the petroleum fuel. The petroleum fuel shall be released by the department from the Stop Sale Order in accordance with Section 525.037, F.S.

(10) Materials. The following materials are hereby incorporated by reference. Copies of these publications may be obtained from ASTM International, 100 Barr Harbor Drive, West Conshohocken, PA 19428, or http://www.astm.org and are also available for public inspection during regular business hours at the Florida Administrative Code and Register, R.A. Gray Building, 500 Building, 500 South Bronough Street, Tallahassee, FL 32399-0250, and at the Florida Department of Agriculture and Consumer Services, Division of Consumer Services, Bureau of Standards, 3125 Conner Boulevard, Tallahassee, FL 32399-1650. Posting of the following materials on the internet for purposes of public examination would violate federal copyright law.

(a) ASTM International Designation D4814-20a (approved April 1, 2020), “Standard Specification for Automotive Spark-Ignition Engine Fuel.”

(b) ASTM International Designation D3699-19 (approved December 15, 2019), “Standard Specification for Kerosine.”

(c) ASTM International Designation D975-20a (approved June 1, 2020), “Standard Specification for Diesel Fuel.”

(d) ASTM International Designation D396-20 (approved June 1, 2020), “Standard Specification for Fuel Oils.”

(e) ASTM International Designation D4806-20 (approved May 1, 2020), “Standard Specification for Denatured Fuel Ethanol for Blending with Gasolines for Use as Automotive Spark-Ignition Engine Fuel.”

(f) ASTM International Designation D5798-20 (approved May 1, 2020), “Standard Specification for Ethanol Fuel Blends for Flexible-Fuel Automotive Spark-Ignition Engines.”

(g) ASTM International Designation D5797-18 (approved December 1, 2018), “Standard Specification for Methanol Fuel Blends (M51-M85) for Methanol-Capable Automotive Spark-Ignition Engines.”

(h) ASTM International Designation D6751-20 (approved January 1, 2020), “Standard Specification for Biodiesel Fuel Blend Stock (B100) for Middle Distillate Fuels.”

(i) ASTM International Designation D7467-20a (approved June 1, 2020), “Standard Specification for Diesel Fuel Oil, Biodiesel Blend (B6 to B20).”

(j) ASTM International Designation D7794-20 (approved July 1, 2020), “Standard Practice for Blending Mid-Level Ethanol Fuel Blends for Flexible-Fuel Vehicles with Automotive Spark-Ignition Engines.”

(k) ASTM International Designation D7862-19 (approved May 1, 2019), “Standard Specification for Butanol for Blending with Gasoline for Use as Automotive Spark-Ignition Engine Fuel.”

Rulemaking Authority 525.14, 570.07(23) FS. Law Implemented 525.01, 525.035, 525.037, 525.14 FS. History–New 1-15-68, Amended 7-1-71, 7-1-73, 12-1-73, 11-16-74, 2-13-80, 5-3-83, Formerly 5F-2.01, Amended 5-3-90, 8-13-92, 11-29-94, 11-13-97, 12-9-98, 8-3-99, 7-31-00, 9-3-01, 8-15-02, 6-29-03, 6-21-04, 4-18-05, 6-1-06, 5-6-08, 1-3-10, 4-3-14, 1-7-15, Formerly 5F-2.001, Amended 11-15-20.

## 5J-21.002 Disposition of Below Standard Gasoline, Kerosene, Diesel Fuels No. 1-D and No. 2-D, and Fuel Oils No. 1 and No. 2, and Alternative Fuels.

(1) Gasoline. All gasoline found not meeting any standard adopted in this rule chapter, or by reason of containing water, sediment, or suspended matter, shall be withheld from sale to the public under the provisions of this section in accordance with the procedures in subsections 5J-21.001(8) and (9), F.A.C.

(2) Kerosene. All kerosene found not meeting any standard adopted in this rule chapter, or by reason of containing visually determinable water, sediment, or suspended matter, shall be withheld from sale to the public under the provisions of this section in accordance with the procedures in subsections 5J-21.001(8) and (9), F.A.C.

(3) Diesel Fuels No. 1-D and No. 2-D. All Diesel Fuel Oils No. 1-D and No. 2-D found not meeting any standard adopted in this rule chapter, or by reason of containing water, sediment, or suspended matter, shall be withheld from sale to the public under the provisions of this section in accordance with the procedures in subsections 5J-21.001(8) and (9), F.A.C.

(4) Fuel Oils No. 1 and No. 2. All Fuel Oils No. 1 and No. 2 found not meeting any standard adopted in this rule chapter, or by reason of containing water, sediment, or suspended matter, shall be withheld from sale to the public under the provisions of this section in accordance with the procedures in subsections 5J-21.001(8) and (9), F.A.C.

(5) Alternative Fuels. All alternative fuels found not meeting any standard adopted in this rule chapter, or by reason of containing water, sediment, or suspended matter, shall be withheld from sale to the public under the provisions of this section in accordance with the procedures in subsections 5J-21.001(8) and (9), F.A.C.

Rulemaking Authority 525.14, 570.07(23) FS. Law Implemented 525.035, 525.037, 525.16 FS. History–New 7-1-71, Amended 7-1-73, Repromulgated 12-31-74, Amended 2-13-80, Formerly 5F-2.02, Amended 5-3-90, 8-13-92, 1-24-93, 11-29-94, 6-1-06, 5-6-08, 1-3-10, 1-7-15, Formerly 5F-2.002, Amended 11-15-20.

## 5J-21.003 Registration and Identification.

(1) Every retail gasoline dispenser shall have the octane rating of the gasoline being sold therefrom conspicuously and firmly posted in a manner conforming with 16 CFR Part 306.12 (1-1-20 Edition), which is hereby incorporated by reference. Copies of this publication may be obtained from the Superintendent of Documents, U.S. Government Publishing Office, 732 N. Capitol Street N.W., Washington, D.C. 20401, or at http://www.flrules.org/Gateway/reference.asp?No=Ref-13980.

(2) Every retail gasoline dispenser shall have the grade designation of the gasoline being sold therefrom conspicuously and firmly attached thereto. The octane rating of gasoline sold using the following grade designations must meet the minimum octane rating indicated:

| Grade Designation | Minimum Octane Rating |
| --- | --- |
| Premium, Super, Supreme, High Test | 91 |
| Midgrade, Plus | 89 |
| Regular, Unleaded | 87 |

(3) All racing gasoline or gasoline designed for special use that is kept, offered, or exposed for sale, or sold at retail that does not meet standards established in subsection 5J-21.001(1), F.A.C.:

(a) May not be advertised or represented, in writing or orally, to be suitable for use in ordinary motor vehicles or boat motors,

(b) Shall be accompanied by a conspicuous sign on the dispenser stating that the product does not meet gasoline specifications.

(4) Every retail kerosene dispenser or container-package of kerosene offered for sale at retail shall be conspicuously labeled “kerosene” immediately followed by the designation: 1-K or 2-K, whichever is applicable.

(5) Every retail diesel fuel dispenser shall be conspicuously labeled “diesel.” The label shall be placed on the vertical surface of each dispenser housing on each side that has measure and price meters. The label shall be on the upper two-thirds of the dispenser and clearly visible to anyone dispensing fuel from the dispenser.

(6)(a) All gasoline kept, offered, or exposed for sale, or sold, at retail, containing at least one percent but no more than 10% by volume of ethanol shall be identified as “contains 10% or less ethanol” or “contains 1-10% ethanol,” or other definitive equivalent statement declaring the presence of ethanol on the upper fifty percent of the dispenser front panel in a position clear and conspicuous from the driver’s position, in a type at least 1/2 inch in height and 1/16 inch stroke (width of type). Gasoline kept, offered, or exposed for sale, or sold, at retail, containing specifically ten percent by volume of ethanol may be identified as “E10” and “contains ethanol” or other definitive equivalent statement declaring the presence of ethanol on the upper fifty percent of the dispenser front panel in a position clear and conspicuous from the driver’s position, in a type at least 1/2 inch in height and 1/16 inch stroke (width of type).

(b) All gasoline kept, offered, or exposed for sale, or sold, at retail, containing at least one percent but no more than 5% by volume of methanol shall be identified as “contains 5% or less methanol” or “contains 1-5% methanol”, or other definitive equivalent statement declaring the presence of methanol on the upper fifty percent of the dispenser front panel in a position clear and conspicuous from the driver’s position, in a type at least 1/2 inch in height and 1/16 inch stroke (width of type).

(c) All gasoline kept, offered, or exposed for sale, or sold, at retail, containing less than 1% ethanol by volume must be dispensed in a manner such that it is not exposed to or blended with any gasoline containing more than 1% ethanol by volume.

(d) Labels placed on any multi-product dispensers must be placed in a position and contain wording so as to clearly and conspicuously identify the presence of ethanol in all such products that contain ethanol. Such labels and placement must not be in such a manner that may suggest products not blended with ethanol contain ethanol. This may be accomplished by use of the words “all gasoline” on the label; specifically identify each product that contains ethanol through language or by arrangement of labels on the dispenser; or through other such clear and conspicuous means.

(7) All alternative fuel kept, offered, or exposed for sale, or sold, at retail that contains more than 15% ethanol or 5% methanol shall be identified by a name indicating the amount of ethanol, or methanol in the fuel and shall be labeled as such on the vertical surface of each dispenser housing on the upper fifty percent of the dispenser front panel in a manner conforming with the layout, type size and setting, color, and label protection requirements of 16 CFR Part 306.12 (1-1-20 Edition), as incorporated by reference in subsection (1) above.

(a) Ethanol mixed with gasoline and containing an ethanol content of 51%-83%, by volume, shall be identified as “51%-83% Ethanol” and “Use Only in Flex-Fuel Vehicles, May Harm Other Engines.”

(b) Methanol mixed with gasoline and containing a methanol content of nominally 51%-85%, by volume, shall be identified as “Methanol Flex Fuel, 51%-85%” and “Use Only in Flex-Fuel Vehicles.” Such fuels shall also contain a label on the vertical surface of each dispenser housing on each side that has measure and price meters and located on the upper fifty percent of the dispenser front panel in a type at least 1/2 inch in height and 1/16 inch stroke (width of type) that reads as follows:

This product contains methanol and may not be suitable for use in all flex-fuel vehicles. Consult with your engine manufacturer or owner’s manual before use.

(c) Ethanol mixed with gasoline and containing an ethanol content greater than that which is permitted in subsection 5J-21.001(1), F.A.C., and less than that which is permitted in subparagraph 5J-21.001(5)(c)1., F.A.C., shall be identified as “XX% Ethanol” and “Use Only in Flex-Fuel Vehicles, May Harm Other Engines” where XX is the ethanol concentration in volume percent rounded to the nearest multiple of 10.

(8)(a) All biodiesel blends containing diesel fuel kept, offered, or exposed for sale, or sold, at retail that contain more than 5% biodiesel shall be identified as “(BXX) Biodiesel Blend,” where XX represents the volume percent biodiesel in the biodiesel blend or “Biodiesel Blend Between 6% and 20%.” All biodiesel or B99 kept, offered, or exposed for sale, or sold, at retail shall be identified as “(BXX) Biodiesel,” where XX represents the volume percent biodiesel. Each dispenser shall be labeled as such on the vertical surface of each dispenser housing on each side that has measure and price meters with a sign clearly visible and located on the upper fifty percent of the dispenser front panel in a type at least 1/2 inch in height and 1/16 inch stroke (width of type).

(b) Every dispenser that dispenses biodiesel or B99 shall contain a label on the vertical surface of each dispenser housing on each side that has measure and price meters and located on the upper fifty percent of the dispenser front panel in a type at least 1/2 inch in height and 1/16 inch stroke (width of type) that reads as follows:

This product contains biodiesel. Consult with your engine manufacturer or owner’s manual before using this product.

(9) All biodiesel blends containing fuel oil kept, offered, or exposed for sale, or sold, at retail that contain more than 5% biodiesel shall be identified as “Fuel Oil Containing Biodiesel (XX),” where XX represents the volume percent biodiesel in the biodiesel blend, and shall be labeled as such on the vertical surface of each dispenser housing on each side that has measure and price meters with a sign clearly visible and located on the upper fifty percent of the dispenser front panel in a type at least 1/2 inch in height and 1/16 inch stroke (width of type). Every dispenser that dispenses a biodiesel blend containing fuel oil with a biodiesel percentage greater than 5% shall contain a label on the vertical surface of each dispenser housing on each side that has measure and price meters and located on the upper fifty percent of the dispenser front panel in a type at least 1/2 inch in height and 1/16 inch stroke (width of type) that reads as follows:

This product contains biodiesel. Consult with your equipment or engine manufacturer or owner’s manual before using this product.

(10) All gasoline containing greater than ten percent ethanol by volume and up to and including fifteen percent ethanol by volume shall be labeled in accordance with 40 CFR 1090.1510 (85 Federal Register 234, December 4, 2020), which is hereby incorporated by reference. Copies of this publication may be obtained from the Superintendent of Documents, U.S. Government Publishing Office, 732 N. Capitol N.W., Washington, D.C. 20401, at https://www.govinfo.gov/content/pkg/FR-2020-12-04/pdf/2020-23164.pdf, or at http://www.flrules.org/Gateway/reference.asp?No=Ref-13982.

(11) Any other alternative fuel shall be labeled clearly and unambiguously on the vertical surface of each dispenser housing on each side that has measure and price meters with a sign clearly visible and located on the upper fifty percent of the dispenser front panel in a type at least 1/2 inch in height and 1/16 inch stroke (width of type).

(12)(a) All gasoline kept, offered, or exposed for sale, or sold, at retail, containing at least one percent but no more than 12.5% by volume of butanol shall be identified as “contains 12.5% or less butanol” or “contains 1-12.5% butanol,” or other definitive equivalent statement declaring the presence of butanol on the upper fifty percent of the dispenser front panel in a position clear and conspicuous from the driver’s position, in a type at least 1/2 inch in height and 1/16 inch stroke (width of type).

(b) Labels placed on any multi-product dispensers must be placed in a position and contain wording so as to clearly and conspicuously identify the presence of butanol in all such products that contain butanol. Such labels and placement must not be in such a manner that may suggest products not blended with butanol contain butanol. This may be accomplished by use of the words “all gasoline” on the label; specifically identify each product that contains butanol through language or by arrangement of labels on the dispenser; or through other such clear and conspicuous means.

Rulemaking Authority 525.14, 570.07(23) FS. Law Implemented 525.01, 525.035, 525.037, 525.14 FS. History–New 12-31-74, Amended 2-13-80, 5-3-83, 4-22-85, Formerly 5F-2.03, Amended 11-28-89, 1-24-93, 11-24-94, 6-1-06, 5-6-08, 1-3-10, 1-7-15, Formerly 5F-2.003, Amended 11-15-20, 2-20-22.

## 5J-21.004 Motor Fuel Price Posting.

(1) Any roadside or other sign, including, but not limited to, prices on poles, monument signs, canopies, ‘A-frame’ signs or other structures, that advertises or displays motor fuel prices and is not connected to a retail motor fuel dispenser as covered in Rule 5J-21.007, F.A.C. must display:

(a) The undiscounted price per gallon for any motor fuel product and applicable grade advertised or displayed on the sign; or

(b) The discounted price per gallon for any motor fuel product and applicable grade advertised or displayed on the sign along with the conditions under which the discount is available, including, but not limited to, “Cash,” “Cash Only,” or “Membership.” The discount conditions must be clearly presented on the sign in a font no less than one-half the size of the largest number posted on the sign and may not be abbreviated. The discount conditions must appear immediately next to, above or below the discounted price and with equal illumination as the discounted price.

(2) All motor fuel prices displayed on the sign must include all applicable taxes and fees.

(3) A business is not required to have a roadside sign nor advertise or display motor fuel prices for all products or grades stored or offered for sale at the retail station, except as required in Rule 5J-21.007, F.A.C.

(4) Failure to comply with the provisions of this rule constitutes a violation of Section 531.44, F.S.

Rulemaking Authority 526.09, 531.41(3), 570.07(23) FS. Law Implemented 526.01, 531.44 FS. History‒New 5-25-15.

## 5J-21.005 Inaccurate Measuring Devices.

(1) For the purpose of Section 525.07, F.S., and this rule, the term “short measure” shall mean the overregistering of fuel by a petroleum fuel measuring device.

(2) If any petroleum fuel measuring device is found to be underregistering fuel in excess of the specifications and tolerances established by the department in Rule 5J-21.007, F.A.C., the inspector shall give in writing the operator or owner of the device up to seven days to fix or adjust the device.

(3) If any petroleum fuel measuring device is found to be overregistering fuel in excess of the specifications and tolerances established by the department in Rule 5J-21.007, F.A.C., the device shall be placed out-of-service by the department through issuance of a Stop Use Order, and prohibited from further use. Such measuring devices placed out-of-service for inaccuracy shall be rendered inoperative either by removal or by the locking of working parts with lead and wire seal and shall not be put back in service without reinspection or the written consent of the department.

(4) All persons and service agencies that repair or install petroleum fuel measuring devices must register with the department on FDACS-10990, Weights and Measures Device Mechanic Registration Application, Rev. 02/17, as incorporated by reference in Rule 5J-22.003, F.A.C. Any such registered person or service agency must immediately notify the department at (850)921-1545, or by email at Standards-Field@fdacs.gov, or by fax at (850)921-1548, after any repairs and/or adjustments to any petroleum measuring devices have been made. Failure of a registered meter mechanic or service agency to notify the department after any repairs and/or adjustments to any petroleum measuring devices that have been made as required is subject to administrative penalties as enumerated in Rule 5J-21.008, F.A.C. In order to make application for registration as an authorized meter mechanic you must:

(a) Maintain a test measure of appropriate size according to the National Institute of Standards and Technology (NIST) Handbook 44, as incorporated by reference in Rule 5J-22.002, F.A.C., that has been calibrated with standards traceable to NIST, pursuant to Section 525.07(9), F.S.

(b) Maintain a sealing iron bearing at least the registered mechanic’s name or initials that are on file with the Department. Use said sealing iron to imprint security seals each time a seal is required to be installed, replaced or affixed.

(c) Have proof of at least one year of experience working as a meter mechanic. If such applicant does not possess one year of experience working as a meter mechanic, the applicant may work for a service agency that repairs or installs petroleum fuel measuring devices that is currently registered with the Department.

(d) Annually apply in person at the Florida Department of Agriculture and Consumer Services, Division of Consumer Services, Bureau of Standards, 2005 Apalachee Parkway, Tallahassee, FL 32399, or submit the following documents to the department via email at Standards-Field@fdacs.gov or by Fax (850-921-1548): FDACS-10990, Weights and Measures Device Mechanic Registration Application, Rev. 02/17, a current calibration report for the test measure(s) meeting the requirement listed in paragraph (4)(a) of this rule, a picture of the sealing iron bearing at least the registered mechanics name or initials, and proof of at least one year of experience working as a meter mechanic or proof of working for a service agency currently registered with the department that repairs or installs petroleum fuel measuring devices. The review of current rules and regulations is also required and shall be accomplished by viewing an online presentation found at https://www.fdacs.gov/Business-Services/Petroleum-Inspection. Information regarding the department-provided presentation may be obtained by contacting the department at (850)921-1545.

(5) Any measuring device that fails to meet applicable requirements, as adopted in this rule chapter, shall be placed out of service by the department through issuance of a Stop Use Order, prohibiting the use of the measuring device.

Rulemaking Authority 525.14, 531.41, 570.07(23) FS. Law Implemented 525.07 FS. History–New 7-1-74, Repromulgated 12-31-74, 5-3-83, Formerly 5F-2.05, Amended 11-29-94, 5-6-08, 1-3-10, 1-7-15, Formerly 5F-2.005, Amended 11-15-20, 2-20-22.

## 5J-21.006 Inspection Identification Stickers.

It shall be the duty of inspectors to affix a sticker to each petroleum measuring device, signifying that the device is inspected by the Department of Agriculture and Consumer Services and that the device owner is responsible for its proper use and maintenance. Stickers shall be placed at such a point upon measuring device where they may be easily read by the public but not at a point where they will interfere with other descriptive material on the device such as figures, lettering or words. It shall be a violation of this rule for any person, unless authorized by the Department, to remove, deface, conceal or in any way obliterate or change this official sticker after it has been affixed by an inspector.

Rulemaking Authority 525.14, 570.07(23) FS. Law Implemented 525.07 FS. History–New 12-31-74, Formerly 5F-2.06, Amended 1-3-10, 1-7-15, Formerly 5F-2.006, Amended 11-15-20.

## 5J-21.007 Adoption of the General Code and the Codes of Liquid-Measuring Devices, Liquefied Petroleum Gas and Anhydrous Ammonia Liquid-Measuring Devices, Hydrocarbon Gas Vapor-Measuring Devices, Vehicle-Tank Meters, Vehicle Tanks Used as Measures of National Institute of Standards and Technology Handbook 44 Meter Sealing Requirements, and Other Related Requirements.

(1) The general code and the codes of liquid-measuring devices, liquefied petroleum gas and anhydrous ammonia liquid-measuring devices, hydrocarbon gas vapor-measuring devices, vehicle-tank meters, and vehicle tanks used as measures relating to specifications, tolerances, and other technical requirements for commercial weighing and measuring devices, contained in National Institute of Standards and Technology Handbook 44, are adopted and incorporated by reference in Rule 5J-22.002, F.A.C.

(2) All operating petroleum fuel measuring devices must be sealed with an appropriate security seal in such a manner that the metering adjustment cannot be changed without breaking the seal. An appropriate security seal is one which has been applied by the Department or a person who is registered with the Department as a meter mechanic and bears at least the name or initials of the registered meter mechanic.

(3) Any registered person, agency, or device owner that has installed or returned to service a petroleum fuel measuring device must report the existence or repair of the petroleum device to the department at (850)921-1545 or by fax at (850)921-1548, within twenty-four (24) hours after installation, but no sooner than 10 days prior to installation using FDACS-03017, Placed in Service Report, Rev. 05/17, as incorporated by reference in Rule 5J-22.003, F.A.C. Petroleum measuring devices placed into service or returned to service by unregistered persons and not in accordance with any exceptions provided by rule shall not be used in commerce.

(4) Each dispensing device from which diesel fuel is sold at retail shall be equipped with a nozzle spout that conforms to SAE International J285, APRIL2019, “Dispenser Nozzle Spouts for Liquid Fuels Intended for Use with Spark Ignition and Compression Ignition Engines,” and is hereby incorporated by reference. Copies of this publication may be obtained at http://standards.sae.org. This code is also available for public inspection during regular business hours at the Florida Administrative Code and Register, R.A. Gray Building, 500 South Bronough Street, Tallahassee, FL 32399-0250, and the Florida Department of Agriculture and Consumer Services, Division of Consumer Services, Bureau of Standards, 3125 Conner Boulevard, Tallahassee, FL 32399-1650. Posting of this material on the internet for purposes of public examination would violate federal copyright law.

(5) All retail motor fuel dispensers in operation at self-service facilities shall comply with the provisions of Section 526.141(5)(b), F.S.

(a) As used in Section 526.141(5)(b), F.S., the term “pump” means the face of a motor fuel dispenser or a stand-alone unit as described in paragraph (b) of this subsection.

(b) The term “affixed,” as used in Section 526.141(5)(b), F.S., means:

1. Directly attached to the pump on the upper fifty percent of the front panel in a position clear and conspicuous from the driver’s position; or

2. Directly attached to a stand-alone unit located no more than 36'' from either side of the motor fuel dispenser, at a height equivalent to the upper fifty percent of the motor fuel dispenser’s front panel, and in a position clear and conspicuous from the driver’s position. If a stand-alone unit is used, it must contain controls to communicate directly with the self-service facility’s staff.

Rulemaking Authority 525.14, 526.09, 526.141(5)(b), 531.40, 531.41(3), 570.07(23) FS. Law Implemented 525.07, 526.141(5)(b), 531.40 FS. History–New 1-1-74, Amended 7-1-74, Repromulgated 12-31-74, Amended 4-18-75, 1-25-76, 1-17-77, 2-15-79, 6-4-80, 4-5-81, 5-2-82, 6-30-83, 7-15-84, 8-11-85, Formerly 5F-2.14, Amended 7-7-86, 4-5-87, 4-27-88, 5-31-89, 8-21-90, 8-5-91, 12-10-92, 11-29-94, 11-13-97, 12-9-98, 8-3-99, 7-31-00, 9-3-01, 8-15-02, 6-29-03, 6-21-04, 6-1-06, 5-6-08, 1-3-10, 1-7-15, Formerly 5F-2.014, Amended 11-10-15, 11-15-20.

## 5J-21.008 Guidelines for Imposing Administrative Penalties.

(1) This rule sets forth the guidelines the department will follow in imposing the penalties authorized under Chapters 525 and 531, F.S. The purpose of the guidelines is to give notice of the range of penalties, which will be imposed for a single violation. These guidelines list aggravating and mitigating factors that, if present, will reduce or increase penalties to be imposed. The guidelines in this rule are based upon a single count violation of each provision listed. Multiple counts of the violated provision or a combination of the listed violations will be added together to determine an overall total penalty and will be grounds for enhancement of penalties.

(2) The department will administratively enforce compliance with Chapters 525 and 531, F.S., and this rule chapter by issuing an administrative complaint, stop sale order, and/or notice of noncompliance for violations of Chapter 525 or 531, F.S., and this rule chapter.

(3) Nothing in this rule shall limit the ability of the department to informally dispose of administrative actions by settlement agreement, consent order, or other lawful means.

(4) Rule Not All-Inclusive. This rule contains illustrative violations. It does not, and is not intended to, encompass all possible violations of the statutes or department rules that might be committed by any person. The absence of any violation from this rule shall in no way be construed to indicate that the violation does not cause harm to the public or is not subject to a penalty.

(5) Aggravating and Mitigating Factors. The department will consider aggravating and mitigating factors in determining penalties for violations of Chapters 525 and 531, F.S., and this rule chapter. The factors shall be applied against each single count of the listed violation.

(a) Aggravating Factors shall include:

1. The violation caused or has the potential to cause harm to a person or property and the degree or extent of such harm.

2. The violation endangered the public safety or welfare.

3. Previous enforcement actions for the same or a similar offense.

4. The violation history over the past three years.

5. The violation existed for more than one month.

6. The violation was repeated within one year.

7. The violator impeded, or otherwise failed to cooperate with the department’s inspection and/or investigation.

8. Previous disciplinary action against the violator in this or any other jurisdiction.

9. Failure to take or initiate affirmative or corrective action within 48 hours after receipt of the stop sale order or within the timeframe specified on a notice of non-compliance for the violation.

10. The violation resulted from an intentional act.

11. The need for repeated follow-up inspections without valid evidence of remedial action taken by the violator.

12. The number of other violations proven in the same proceeding.

13. The benefit to the violator.

(b) Mitigating Factors shall include:

1. Any documented efforts by the violator at rehabilitation.

2. The intentional actions of another party prevented the violator from complying with the applicable laws or rules.

3. Documented financial hardship.

4. Acts of God or nature that impairs the ability of the violator to comply with Chapter 525 or 531, F.S. or this rule chapter.

5. The violator expeditiously took affirmative or corrective action after it received written notification of the violation, including costs incurred by the violator for rectifying any damage or harm to consumers’ vehicles and/or property.

6. The disciplinary history of the violator and with consideration of whether three years have passed since the previous violation.

7. A statement, in writing, provided to the department declaring clear and unequivocal acceptance of responsibility for a first violation within a three-year period.

(6) Penalties.

(a) Notice of Noncompliance. Any department investigation or inspection which reveals violations listed in this subsection of this rule in which the department determines that the violator was unaware of the rule or unclear as to how to comply with it will result in the issuance of a notice of noncompliance as the department’s first response to the violation. For the purposes of this rule, the following violations shall result in the issuance of a notice of noncompliance:

1. Violations to subsection 5J-21.007(1), F.A.C., where the violation has a low potential for causing economic or physical harm to a person; adversely affecting the public health, safety, or welfare; or creating a significant threat of such harm, if left uncorrected.

2. Violations to Rule 5J-22.003, F.A.C., pertaining to petroleum products and applications, where the violation has a low potential for causing economic or physical harm to a person; adversely affecting the public health, safety, or welfare; or creating a significant threat of such harm, if left uncorrected.

3. Misrepresentation of the price of petroleum fuel on a display, a violation of Section 531.44, F.S.

4. Violations of subsection 5J-21.005(2), F.A.C.

5. Violations of subsections 5J-21.007(3) or (4), F.A.C.

6. Violations of subsection 5J-21.001(6), F.A.C.

7. Gasoline blended with ethanol or butanol found to have an ethanol or butanol content of more than one (1.0%) percent by volume below the posted ethanol or butanol content displayed on the dispenser or gasoline found to have less than one (1.0%) percent by volume ethanol or butanol that is labeled as containing ethanol or butanol.

8. Diesel fuel blended with biodiesel found to have a biodiesel content of more than two (2.0%) percent by volume below the posted biodiesel content displayed on the dispenser.

9. A mid-level ethanol blend found to have an ethanol content of more than five (5.0%) percent by volume below the posted ethanol content displayed on the dispenser or found to have less than the amount of ethanol permitted under paragraph 5J-21.001(1)(c), F.A.C.

(b) Tier I Major Violations. A violation of Chapter 525 or 531, F.S., or this rule chapter is a Tier I violation if it does not result in economic or physical harm to a person or adversely affect the public health, safety, or welfare or create a significant threat of such harm. Tier I violations shall result in the issuance of a Stop Sale Order or a Stop Use Order. Discovery of a repeat violation within a three-year period shall result in the imposition of an administrative fine not to exceed the statutory maximum set forth in Section 525.16, F.S. For the purposes of this rule, the following violations shall be considered Tier I violations:

1. Gasoline with an octane rating difference of more than one (1.0), but not more than two (2.0) below the octane rating ((R+M)/2) displayed on the dispenser.

2. Gasoline blended with ethanol up to 10%, by volume, or butanol up at 12.5%, by volume, found to have an ethanol or butanol content of more than one (1.0%) percent by volume, but not more than three (3.0%) percent by volume, above the posted ethanol or butanol content displayed on the dispenser.

3. Gasoline found not in compliance because of a silver corrosion rating of two (2) as incorporated through the adopted version of ASTM International Designation D4814, “Standard Specification for Automotive Spark-Ignition Engine Fuel” in paragraph 5J-21.001(10)(a), F.A.C.

4. Gasoline found not in compliance from June 1 through September 15 because of a vapor pressure of up to and including 11.0 psi as incorporated through the adopted version of ASTM International Designation D4814, “Standard Specification for Automotive Spark-Ignition Engine Fuel” in paragraph 5J-21.001(10)(a), F.A.C.

5. Kerosene found not in compliance by reason of color.

6. Diesel fuel No. 2-D found not in compliance with the flash point standard, but above 100 °F.

7. Diesel fuels No. 1-D and No. 2-D found not in compliance with the ultra-low (S15) sulfur standard, but equal to or below 35 ppm sulfur.

8. A biodiesel blend found to have a biodiesel content of more than two (2.0%) percent by volume, but not more than five (5.0%) percent by volume, above the posted biodiesel content displayed on the dispenser.

9. A biodiesel blend (with No. 2-D diesel fuel) found not in compliance with the flash point standard, but above 100 °F.

10. Biodiesel and biodiesel blends found not in compliance with the ultra-low (S15) sulfur standard, but equal to or below 35 ppm sulfur.

11. Violations of paragraph 5J-21.003(6)(d), F.A.C.

12. The following violations shall result in the removal of affected equipment from service.

a. Indicator inoperable or unreadable.

b. Indicator advancing when the device is activated.

c. Air eliminator missing or inoperable.

d. Inoperative interlock.

e. Indicator movement without nozzle activation.

f. Meter over-registering more than six cubic inches.

g. Incorrect indicator.

h. Operating a meter without an appropriate security seal or improperly sealed.

i. Leaking swivel.

j. Exposed electrical wires.

k. Leaking filter.

l. Leaking impact valves.

m. Leaking vapor pump.

n. Leaking nozzle.

o. Impact valve inoperable.

p. Leaking meter.

q. Incorrect dispenser type for product being dispensed.

r. Leaking dispenser hose.

s. Violations of subsection 5J-21.005(3), F.A.C.

t. Violations of Rule 5J-21.006, F.A.C.

u. Any violations to subsection 5J-21.007(1), F.A.C., where the device and/or equipment is required to be immediately removed from service due to the potential for causing economic or physical harm to a person; due to the potential for adversely affecting the public health, safety, or welfare; or due to the potential to create a significant threat of such harm, if left uncorrected.

v. Any violations to Rules 5J-22.002 and 5J-22.003, F.A.C., pertaining to petroleum products and applications, where the device and/or equipment is required to be immediately removed from service due to the potential for causing economic or physical harm to a person; due to the potential for adversely affecting the public health, safety, or welfare; or due to the potential to create a significant threat of such harm, if left uncorrected.

(c) Tier II Major Violations. A violation of Chapter 525 or 531, F.S., or this rule chapter is a Tier II violation if it results in economic or physical harm to a person or adversely affects the public health, safety, or welfare or creates a significant threat of such harm. Tier II violations shall result in prohibiting the sale, distribution, offering for sale or distribution of the substandard product and imposition of an administrative fine not to exceed the statutory maximum set forth in Section 525.16, F.S. For the purposes of this rule, the following violations shall be considered Tier II violations:

1. Failure to meet the volatility requirements for gasoline blended with ethanol as specified in subparagraphs 5J-21.001(1)(a)1. or 2., F.A.C.

2. Failure to meet the vapor pressure requirements for gasoline (including gasoline blended with oxygenates); including, if greater than 11.0 psi from the time period June 1, through September 15.

3. Failure to meet the minimum anti-knock index (AKI) or octane rating requirements for gasoline (including gasoline blended with oxygenates); specifically, gasoline found to be more than two (2) less than the posted rating.

4. Violations of paragraphs 5J-21.001(1)(c), (d), or (e), F.A.C.

5. Failure to match the posted ethanol or butanol content for gasoline blended with ethanol up to 10% by volume or butanol up to 12.5% by volume; specifically, when the ethanol or butanol content is found to be more than three (3.0%) percent by volume above the posted ethanol or butanol content (percentage by volume).

6. Failure to meet the silver corrosion standard for gasoline (including gasoline blended with oxygenates); specifically, when the rating is greater than two (2).

7. Failure to meet the flash point requirements for No. 2 diesel fuels and biodiesel blends (with No. 2 diesel fuels); specifically, when the flash point is found to be less than 100 °F.

8. Failure to meet the sulfur requirements for ultra-low sulfur diesel (ULSD) fuels and biodiesel blends (with ULSD fuels); specifically, when the sulfur content is found to be greater than 35 ppm.

9. Violations of subparagraph 5J-21.001(5)(d)2., F.A.C., pertaining to the maximum biodiesel content allowed in biodiesel blends (with diesel fuels or fuel oils).

10. Failure to match the posted biodiesel content for biodiesel blends (with diesel fuels or fuel oils); specifically, when the biodiesel content is found to be more than five (5.0%) percent by volume above the posted biodiesel content (percentage by volume).

11. Any fuel found below standard by reason of containing water, sediment, and/or suspended matter.

12. Failure to meet any other requirements listed in the standards for gasoline (including gasoline blended with oxygenates), as incorporated through the adopted version of ASTM International Designation D4814, “Standard Specification for Automotive Spark-Ignition Engine Fuel” in paragraph 5J-21.001(10)(a), F.A.C., not already listed is this section.

13. Failure to meet any other requirements listed in the standards for kerosene (kerosine), as incorporated through the adopted version of ASTM International Designation D3699, “Standard Specification for Kerosine” in paragraph 5J-21.001(10)(b), F.A.C., not already listed in this section.

14. Failure to meet any other requirements listed in the standards for diesel fuel No. 1-D and No. 2-D, as incorporated through the adopted version of ASTM International Designation D975, “Standard Specification for Diesel Fuel” in paragraph 5J-21.001(10)(c), F.A.C., not already listed in this section.

15. Failure to meet any other requirements listed in the standards for fuel oils No. 1 and No. 2, as incorporated through the adopted version of ASTM International Designation D396, “Standard Specification for Fuel Oils” in paragraph 5J-21.001(10)(d), F.A.C., not already listed in this section.

16. Failure to meet any requirements listed in the standards for denatured fuel ethanol, as incorporated through the adopted version of ASTM International Designation D4806, “Standard Specification for Denatured Fuel Ethanol for Blending with Gasolines for Use as Automotive Spark-Ignition Engine Fuel” in paragraph 5J-21.001(10)(e), F.A.C.

17. Failure to meet any other requirements listed in the standards for Ethanol Fuel Bends (51 to 83 volume percent ethanol), as incorporated through the adopted version of ASTM International Designation D5798, “Standard Specification for Ethanol Fuel Blends for Flexible-Fuel Automotive Spark-Ignition Engines” in paragraph 5J-21.001(10)(f), F.A.C., not already listed in this section.

18. Failure to meet any other requirements listed in the standards for Methanol Fuel Blends (51 to 85 volume percent methanol), as incorporated through the adopted version of ASTM International Designation D5797, “Standard Specification for Methanol Fuel Blends (M51-M85) for Methanol-Capable Automotive Spark-Ignition Engines” in paragraph 5J-21.001(10)(g), F.A.C., not already listed in this section.

19. Failure to meet any requirements listed in the standards for biodiesel fuel blend stock (or biodiesel), as incorporated through the adopted version of ASTM International Designation D6751, “Standard Specification for Biodiesel Fuel Blend Stock (B100) for Middle Distillate Fuels” in paragraph 5J-21.001(10)(h), F.A.C.

20. Failure to meet any other requirements listed in the standards for biodiesel blends (with diesel fuel), as incorporated through the adopted version of ASTM International Designation D7467, “Standard Specification for Diesel Fuel Oil, Biodiesel Blend (B6 to B20)” in paragraph 5J-21.001(10)(i), F.A.C., not already listed in this section.

21. Failure to meet any other requirements listed in the standards for biodiesel blends (with fuel oil), as incorporated through the adopted version of ASTM International Designation D396, “Standard Specification for Fuel Oils” in paragraph 5J-21.001(10)(d), F.A.C., not already listed in this section.

22. Failure to meet any other requirements listed in the standards for mid-level ethanol blends, as incorporated through the adopted version of ASTM International Designation D7794, “Standard Practice for Blending Mid-Level Ethanol Fuel Blends for Flexible-Fuel Vehicles with Automotive Spark-Ignition Engines” in paragraph 5J-21.001(10)(j), F.A.C., not already listed in this section.

23. Failure to match the posted ethanol content for mid-level blends; specifically, when the ethanol content is found to be more than five (5.0) percent by volume above the posted ethanol content.

24. Violations of paragraphs 5J-21.003(6)(a), (b), or (c), F.A.C.

25. Violations of subsection 5J-21.003(7), F.A.C.

26. Violations of subsection 5J-21.003(10), F.A.C.

27. Violations of subsection 5J-21.005(4), F.A.C.

28. Violations of subsection 5J-21.007(2), F.A.C.

29. Failure to correct violations of law, rule, or adopted sections of NIST Handbook 44, as incorporated by reference in Rule 5J-22.002, F.A.C., or NIST Handbook 130 (pertaining to petroleum measuring devices, as incorporated by reference in Rule 5J-22.003, F.A.C.) within the time period specified in a notice of non-compliance. Any device affected by a correction notice issued pursuant to this rule that is not corrected within the time period specified shall be removed from service until such time that the deficiency has been corrected.

30. Failure to meet any requirements listed in the standards for butanol, as incorporated through the adopted version of ASTM International Designation D7862, “Standard Specification for Butanol for Blending with Gasoline for Use as Automotive Spark-Ignition Engine Fuel” in paragraph 5J-21.001(10)(k), F.A.C.

(d) Willful Violations. Any willful and intentional violation of Chapter 525 or 531, F.S., or this rule chapter or of any requirement or standard adopted pursuant thereto, shall result in the imposition of an administrative fine of up to $5,000 per violation. Willful violations shall include the following:

1. The unauthorized breaking, cutting, or removal of any seal applied by the department;

2. The sale or distribution, or offering for sale or distribution, of any petroleum fuel under stop sale order;

3. The sale or distribution, or offering for sale or distribution, of any petroleum fuel that was previously placed under a stop sale order and that has not been made to conform to standard; and

4. Violations which result from a failure to comply with a final order, a notice of non-compliance, a stop sale order, or any condition stipulated on a release of a stop sale order.

(7) Resolution of Alleged Violations, Settlement, and Additional Enforcement Remedies.

(a) Failure to respond to an administrative complaint shall result in the entry of a default final order against the violator or entity responsible for the violation. The department shall impose administrative fines in a default final order equal to the maximum amount as allowable under Section 525.16(1)(a), F.S.

(b) A failure to comply with either a final order or a default final order of the department shall result in any applicable registration revocation and an administrative fine equal to the maximum amount as allowable under Section 525.16(1)(a), F.S. Additional penalties shall be sought through the enforcement of the order in circuit court.

Rulemaking Authority 525.14, 531.41, 570.07(23) FS. Law Implemented 525.16, 531.42, 531.44, 570.971(4) FS. History–New 2-24-00, Amended 7-30-02, 6-1-06, 5-6-08, 1-3-10, 1-7-15, Formerly 5F-2.016, Amended 11-15-20.

## 5J-21.009 Security Measures for Petroleum Fuel Measuring Devices.

(1) As used in Section 525.07(10)(a)1., F.S., “pressure-sensitive security tape” means tape that is irreversibly broken, destroyed, or watermarked as voided if removed or attempted to be removed after application. Pressure-sensitive security tape does not include tape that is capable of being reused after its initial application.

(2) As used in Section 525.07(10)(a)4., F.S., “physical locking mechanism” means a uniquely marked high security lock such as a disc type padlock, a high security bezel lock, or a padlock that has a hardened shackle and shackle guard and for which documentation is presented showing that it has been independently tested and found to meet or exceed Central European Norm (CEN) 4.

(3) Each person who owns or operates a retail petroleum fuel measuring device shall have affixed to or installed onto the measuring device at least two security measure to restrict the unauthorized access of customer payment card information. Pursuant to Section 525.07(10)(a)8., F.S., the department shall consider proposed security measures not explicitly authorized by statute and shall approve those found to be at least as restrictive as any one of the security measures listed in Section 525.07(10)(a), F.S.

(4) Each person who owns or operates a retail petroleum fuel measuring device and who wishes to use a security measure not listed in Section 525.07(10)(a), F.S., shall submit FDACS-03577, Request for Approval of Alternative Security Measure, Rev. 12/21, hereby incorporated by reference. A copy of this form may be accessed at http://www.flrules.org/Gateway/reference.asp?No=Ref-13981.

(5) Within 30 days of receipt of FDACS-03577, Request for Approval of Alternative Security Measure, Rev. 12/21, incorporated by reference in subsection (4) of this rule, the department shall provide written notification to the owner or manager whose contact information appears on the request that the request has been granted or denied, or that the request does not provide enough information. If the request does not provide enough information for the department to determine whether the proposed security measure should be approved, the department shall notify the owner or manager whose contact information appears on the request that additional information is required. Failure to provide additional information within 30 days of notification shall result in the denial of the request for approval.

(6) In determining whether a proposed alternative security measure restricts unauthorized access of customer payment card information, the department will consider the following:

(a) The physical, technological, and/or data security provided by the proposed security measure;

(b) The ease with which the proposed security measure can be breached;

(c) The means by which the proposed security measure can be verified by a department inspector;

(d) The expected level of maintenance required to maintain the effectiveness of the proposed security measure; and,

(e) The onsite and/or remote maintenance plan that will be used to ensure the proposed security measure has not been breached.

(7) The department’s approval of an alternative security measure applies only to those locations indicated in the approved request submitted by an owner or operator. An approved alternative security measure that fails to restrict the unauthorized access of customer payment card information shall be revoked in accordance with Section 120.60, F.S. If an owner or operator wishes to use an identical, department-approved alternative security measure at additional locations, the original request for approval may be supplemented by providing the information required by sections 1.-4. of FDACS-03577, Request for Approval of Alternative Security Measure, Rev. 12/21, incorporated by reference in subsection (4) of this rule.

(8) No security measure affixed or installed in accordance with Section 525.07(10), F.S., or this rule shall obstruct the department’s access to the measuring device for inspection purposes.

(9) If any petroleum fuel measuring device is found without the security measures required by Section 525.07(10), F.S., or with an illegal skimming or filtering device or an altered or damaged security measure, the device shall be placed out of service by the department through the issuance of a Stop Use Order, and prohibited from further use until documentation confirming the installation, replacement, or repair of the security measure(s) is received by the department and a Release is issued.

Rulemaking Authority 525.07(10)(g), 525.14, 570.07(23) FS. Law Implemented 525.07, 525.08, 570.07(16)(h) FS. History–New 10-5-16, Amended 2-20-22.