15C-5.003 Minimum Requirements for Official Vehicle Inspection Station; (Public).

SPACE REQUIREMENTS

(1) Entrance 14' wide × 14' high × 45' deep for each individual inspection lane. Exceptions may be made on multi-lane stations which must have at least one lane meeting above requirements. The Department may make other exceptions as it deems necessary.

(2) Entire space must be in a permanent type building with two permanent walls and permanent roof. Temporary expedients such as tents, arbors, or sheds are not acceptable.

(3) The floor of the building must be leveled, hard-surfaced, and of any material except dirt. Wood floors which sag under the vehicles’ weight are not acceptable.

(4) Each area of the building used for inspecting must be approved by the Department Facility Examiner.

(5) The complete inspection shall be conducted with the entire vehicle inside the approved building in an approved and marked inspection area (except tests made with decelerometer), except that vehicles which are too large to get inside the building door shall be inspected as close as possible to the approved inspection area.

Specific Authority 325.26 FS. Law Implemented 325.20 FS. History–New 5-7-81, Formerly 15C-5.03.