## 20-39.008 Grapefruit – Approved Sizes, and Pack for Determining Sizes in Standard Carton.

(1) For determining size when grapefruit is place-packed for shipment, fruit shall be placed in standard 4/5 bushel container number DOC-01-P, utilizing the following pack, count and diameter range:

| Size and Count | Pack | Rows | Layers | Diameter Range in Inches |
| --- | --- | --- | --- | --- |
| 14* | 2 x 1 | 3 | 3 | 9/16 |
| 18 | 2 x 2 | 3 | 3 | 9/16 |
| 23 | 3 x 2 | 3 | 3 | 9/16 |
| 27 | 3 x 3 | 3 | 3 | 8/16 |
| 32 | 4 x 3 | 3 | 3 | 8/16 |
| 36 | 4 x 4 | 3 | 3 | 8/16 |
| 40 | 4 x 5 | 3 | 3 | 8/16 |
| 48 | 3 x 3 | 4 | 4 | 7/16 |
| 56 | 4 x 3 | 4 | 4 | 7/16 |
| 64 | 4 x 4 | 4 | 4 | 7/16 |

*Size 14 may be packed in a layer pack with 6 fruit in the bottom layer, 2 fruit in a second layer, and 6 fruit in the top layer.

Actual count shall be shown on the container if size and count are the same. Otherwise, both the size and minimum count shall be shown on the container.

(2) When grapefruit is not place-packed, the sizes and respective diameter ranges as shown in subsection 20-39.008(1), F.A.C., shall apply.

(3) For diameter range and off-size tolerances refer to 7 C.F.R. part 51.761, United States Standards for Grades for Florida Grapefruit as amended August 1, 1996.

(4) In order to allow for variations incident to proper packing, not more than 5% of the containers, if “place-packed,” or not more than 10% of the containers, if “volume-filled,” in any lot may fail to meet requirements for count or pack arrangements or well-filled as prescribed in 7 C.F.R. part 51.762, United States Standards for Grades of Florida Grapefruit as amended August 1, 1996.

(5) For determining size, fruit in a place-packed container shall be considered properly sized and the carton well-filled when at least one-half of the top layer of fruit are not more than one-half inch below the top or two inches above the top of a standard container (DOC-01-P).

Rulemaking Authority 601.10(1), (7), 601.11, 601.18(5) FS. Law Implemented 601.02(4), (5), 601.10(7), 601.11, 601.18(5) FS. History–Formerly 105-1.03(1)(b), (3), Amended 1-1-75, 1-1-75, 4-15-75, 8-1-75, 3-16-80, Formerly 20-39.08, Amended 12-27-92, 5-23-93, 10-13-96.