61C-5.004 Bulletin Boards.

(1) Bulletin boards and frames used in elevator cars shall not create any conditions which will be unsafe for user of the elevator car. Users shall include:

(a) Disabled persons;

(b) Persons confined to wheelchairs, and

(c) All other persons who may operate the elevator car in its normal course of use.

(2) Bulletin boards shall not protrude more than 1 inch beyond the vertical line of the car wall. They shall not encroach on any clearances required to be maintained in the elevator by Chapter 399, Florida Statutes, and ASME A17.1.

(3) Bulletin boards shall be framed and all edges must be smooth and rounded. No sharp edges of any kind shall protrude.

(4) A glass or plastic cover shall be provided. Glass, if used, must meet the following requirements:

(a) Be laminated;

(b) Meet the requirement for laminated glass as set forth in ANSI Z97.1;

(c) The cover shall be securely held in place by the frame.

(5) The frame and bulletin board shall be permanently fastened to the car wall in such a manner so that all parts including the cover in place will withstand any and all tests required of the elevator.

(6) All materials used shall be fire resistive equal to the requirements of the cab enclosure.

(7) The bottom of the bulletin boards shall not be less than 4 feet above the cab floor, and no less than three inches above a handrail. The total area shall not exceed 4 square feet.

Specific Authority 399.02 FS. Law Implemented 399.02(2) FS. History–New 5-14-79, Amended 8-1-82, Formerly 7C-5.04, Amended 10-31-88, 4-11-91, Formerly 7C-5.004, Amended 2-2-94, 10-4-00.