62-25.020 Definitions.

(1) “Artificial Watercourse” means a man-made waterway that was totally dredged or excavated prior to October 1, 1984 and which connects formerly isolated, nonjurisdictional wetlands to other waters. The Department shall bear the burden to show that such artificial watercourse was not totally dredged or excavated or that the connected wetlands were formerly jurisdictional.

(2) “Completion of Construction” means the time at which the stormwater discharge facility is first placed into operation or when the project passes final building inspection or when the project receives a certificate of occupancy, whichever comes first.

(3) “Conservation Plan” means a formal document, prepared or approved by a local Soil and Water Conservation District Board organized pursuant to Chapter 582, F.S., which outlines a system of management practices to control soil erosion, reduce sediment loss or protect the water quality on a specific parcel of property.

(4) “Construction” means any on-site activity which will result in the creation of a new stormwater discharge facility, including the building, assembling, expansion, modification or alteration of the existing contours of the property, the erection of buildings or other structures, or any part thereof, or land clearing.

(5) “Detention” or “To Detain” means the collection and temporary storage of stormwater in such a manner as to provide for treatment through physical, chemical, or biological processes with subsequent gradual release of the stormwater.

(6) “Engineer” means a Professional Engineer registered in Florida, or other person exempted pursuant to the provisions of Chapter 471, F.S., who is competent in the fields of hydrology and stormwater pollution control.

(7) “Effective Grain Size” means the diameter of filter sand or other aggregate that corresponds to the 10 percentile finer by dry weight on the grain size distribution curve.

(8) “Filtration” or “To Filter” means the selective removal of suspended matter from stormwater by passing the water through at least 2 feet of suitable fine textured granular media such as porous soil, uniformly graded sand and gravel, or other natural or artificial aggregate, which may be used in conjunction with filter fabric and/or underdrain pipe.

(9) “Intermittent Watercourse” means a stream or waterway that flows only at certain times of the year, flows in direct response to rainfall, and is normally an influent stream except when the groundwater table rises above the normal wet season level.

(10) “New Stormwater Discharge Facility” means a stormwater discharge facility which was not in existence on February 1, 1982, or for which a completed stormwater discharge, dredge or fill, or other Department permit or license application had not been received before February 1, 1982, or an existing stormwater discharge facility which is modified, as specified in subsection 62-25.040(3), F.A.C., on or after February 1, 1982. A stormwater discharge facility approved or found to be exempt by the Department before February 1, 1982, or a facility which had been determined by the Department not to be significant pursuant to subsection 62-4.248(5), F.A.C., before February 1, 1982, or a facility exempted pursuant to subsection 62-25.030(2), F.A.C., shall not be considered a new stormwater discharge facility unless modified pursuant to subsection 62-25.040(3), F.A.C.

(11) “Regional Stormwater Discharge Facility” means a stormwater discharge facility which is permitted pursuant to subsection 62-25.040(6), F.A.C., and is designed and constructed to accept stormwater from multiple parcels within the drainage area served by the regional facility. Drainage area refers to the land or development that is served by and/or contributes stormwater to the regional facility.

(12) “Retention” or “To Retain” means the prevention of, or to prevent the discharge of, a given volume of stormwater runoff into surface waters of the State by complete on-site storage.

(13) “Stormwater” means the flow of water which results from, and which occurs immediately following, a rainfall event.

(14) “Stormwater Discharge Facility” means a stormwater management system which discharges stormwater into surface waters of the State.

(15) “Stormwater Management System” means the designed features of the property which collect, convey, channel, hold, inhibit or divert the movement of stormwater.

(16) “Swale” means a manmade trench which:

(a) Has a top width-to-depth ratio of the cross-section equal to or greater than 6:1, or side slopes equal to or greater than 3 feet horizontal to 1 foot vertical; and,

(b) Contains contiguous areas of standing or flowing water only following a rainfall event; and,

(c) Is planted with or has stabilized vegetation suitable for soil stabilization, stormwater treatment, and nutrient uptake; and,

(d) Is designed to take into account the soil erodibility, soil percolation, slope, slope length, and drainage area so as to prevent erosion and reduce pollutant concentration of any discharge.

(17) “Uniformity Coefficient” means the number representing the degree of homogeneity in the distribution of particle sizes of filter sand or other granular material. The coefficient is calculated by determining the D60 /D10 ratio where D10 and D60 refer to the particle diameter corresponding to the 10 and 60 percentile of the material which is finer by dry weight.

(18) “Waters” are as defined in Section 403.031(13), F.S.

(19) “Wetlands” means, for the purposes of this rule, those waters which are dominated by those plant species listed in Rule 62-301.400, F.A.C., and which meet the conditions specified in subsection 62-25.042(2), F.A.C.

(20) “Wetlands Stormwater Discharge Facility” means a new stormwater discharge facility which incorporates those wetlands identified in subsection 62-25.042(2), F.A.C., into the stormwater management system to provide stormwater treatment.

Specific Authority 373.026(7), 373.043, 373.4145, 403.805(1) FS. Law Implemented 373.4145 FS. History–Formerly 17-4.248, Amended and Renumbered 2-1-82, Amended 3-30-82, 1-26-84, 5-8-85, Formerly 17-25.02, 17-25.020.