62-640.100 Scope, Intent, Purpose, and Applicability.

(1) All domestic wastewater treatment facilities which use biological treatment processes generate domestic wastewater residuals as a by-product of the treatment process. The Department finds that unregulated use, disposal, or land application of these residuals poses a threat to the environment and public health. It is the intent of the Department in this chapter to regulate the management, use, and land application of residuals so as to ensure protection of the environment and public health.

(2) The Department also intends in this chapter to encourage the beneficial use of residuals.

(3) This chapter establishes minimum requirements for residuals which are to be applied to land for agricultural purposes, distributed and marketed, or used for land reclamation. Included are residuals which are composite with yard trash, wood chips, or similar bulking agents and ultimately applied to land or distributed and marketed.

(4) This chapter also establishes minimum requirements for septage which will be treated at facilities permitted by the Department and will be applied to land for agricultural purposes or land reclamation.

(5) The purpose of Chapter 62-640, F.A.C., is to provide minimum standards for the treatment of residuals and septage to be applied to land or distributed and marketed, establish land application criteria, and define requirements for agricultural operations which have received or will receive residuals or septage.

(6) Applicability.

(a) Requirements in this chapter shall apply to domestic wastewater treatment facilities, residuals management facilities, and septage management facilities that generate residuals or septage which are to be applied to agricultural sites or reclamation sites, or which are distributed and marketed.

(b) The requirements in this chapter shall also apply to appliers or distributors of residuals or residuals products, and to owners or operators of agricultural sites or reclamation sites which receive residuals.

(c) Unless specifically provided otherwise in this chapter, requirements in this chapter shall apply to all facilities which generate residuals or apply residuals to agricultural sites or reclamation sites, or which distribute and market residuals or operate an agricultural site or reclamation site, for which complete permit applications were received after December 1, 1997.

(d) Unless specifically provided otherwise in this chapter, requirements in this chapter shall apply to all septage management facilities that treat more than 10,000 gallons per day monthly average daily flow or more than 20,000 gallons in a single day, and that apply septage to agricultural sites or reclamation sites. The requirements of this chapter shall also apply to appliers of septage, and to operators or owners of an agricultural site or reclamation site which has had septage from facilities permitted under this chapter applied to the land after December 1, 1997.

(e) Unless specifically provided otherwise in this chapter, requirements in this chapter that apply to residuals shall also apply to septage from facilities regulated by the Department, and to products derived from such septage, or residuals, or combinations thereof.

(f) Unless specifically provided otherwise in this chapter, requirements in this chapter shall apply to composting facilities, as defined by this chapter, which use yard trash, wood chips, or similar bulking agents, and apply the resulting compost to land or distribute and market the resulting compost after December 1, 1997.

(g) Facilities which have submitted a complete wastewater permit application or which have received an initial permit before December 1, 1997, are considered to be existing facilities and shall meet the requirements of this chapter in accordance with paragraph (h) below.

(h) Existing facilities in Florida shall comply with these requirements at the time of renewal or substantial revision of the wastewater permit, whichever occurs first. Existing facilities may choose to comply with the requirements of this chapter prior to the time specified in this rule by obtaining a permit revision under Chapter 62-620, F.A.C.

(i) Until such time as the wastewater permit is renewed or a new permit is issued for expansion or substantial modification of the facility, the facility shall comply with the requirements for land application of residuals or septage in the existing permit.

(j) Residuals or residuals products which are generated outside of Florida but imported to Florida are subject to the provisions of this chapter beginning December 1, 1997.

(k) The following activities are excluded from the requirements of this chapter:

1. Regulation of septage management facilities that treat 10,000 gallons per day or less on a monthly average daily flow basis and no more than 20,000 gallons in a single day. These facilities are regulated by the Department of Health in accordance with Chapter 64E-6, F.A.C.

2. Land application of septage treated by facilities which are regulated by the Department of Health in accordance with Chapter 64E-6, F.A.C.

3. Disposal of residuals, septage, and other solids in a solid waste landfill. Disposal of these materials shall be in accordance with Chapter 62-701, F.A.C.

4. Disposal of residuals by placement on land for purposes other than soil conditioning or fertilization, such as at a monofill, surface impoundment, waste pile, or dedicated site. Disposal in such cases shall be in accordance with Chapter 62-701, F.A.C.

5. Incineration of residuals. Incineration of residuals shall meet the requirements of Chapters 62-210, 62-212, 62-213, 62-272, 62-273, 62-275, 62-296, and 62-297, F.A.C., and the Resource Conservation and Recovery Act.

6. Co-composting of residuals with solid waste other than yard trash, wood chips or similar bulking agents. Co-composting of residuals with other solid waste materials shall be in accordance with Chapter 62-709, F.A.C.

7. Treatment, management, or disposal of industrial sludges or septage, air treatment sludges, and water supply treatment sludges.

8. Disposal of screenings and grit from the preliminary treatment components of wastewater treatment facilities, solids from sewer line cleaning operations, and solids from lift stations and pump stations. Disposal of these materials shall be in accordance with Chapter 62-701, F.A.C.

Specific Authority 403.051, 403.061, 403.062, 403.087, 403.088, 403.704, 403.707 FS. Law Implemented 403.021, 403.051, 403.061, 403.087, 403.088, 403.0881, 403.702, 403.704, 403.707, 403.708 FS. History–New 8-12-90, Formerly 17-640.100, Amended 3-30-98.