62-770.200 Acronyms and Definitions.

All words and phrases defined in Section 376.301, F.S., shall have the same meaning when used in this chapter unless specifically stated otherwise in this chapter. The following words and phrases used in this chapter shall, unless the context clearly indicates otherwise, have the following meanings:

(1) “Action level” means a specified concentration of a petroleum products’ contaminant of concern that, if exceeded during natural attenuation monitoring or post active remediation monitoring, may require additional site assessment or active remediation. Action levels are established during the approval process for Natural Attenuation Monitoring Plans pursuant to Rule 62-770.690, F.A.C., and Post Active Remediation Monitoring Plans pursuant to Rule 62-770.750, F.A.C., and are not equivalent to CTLs.

(2) “Additive effect” means a scientific principle that the toxicity that occurs as a result of exposure is the sum of the toxicities of the individual chemicals to which an individual is exposed.

(3) “Antagonistic effect” means a scientific principle that the toxicity that occurs as a result of exposure is less than the sum of the toxicities of the individual chemicals to which an individual is exposed.

(4) “Apportioned” means the adjustment of CTLs such that for non-carcinogenic petroleum products’ contaminants of concern that affect the same target organ(s), the hazard index (sum of the hazard quotients) is 1 or less, and for carcinogens, the cumulative lifetime excess cancer risk level is 1.0E-6, as applicable.

(5) “Background concentrations” means concentrations of petroleum products’ contaminants of concern that are naturally occurring in the groundwater, surface water, soil, or sediment in the vicinity of the site.

(6) “Best achievable detection limit” means the practical quantitation limit. [Refer to the PQL guidelines referenced in subsection 62-770.140(5), F.A.C., for guidance.]

(7) “Cleanup target level” (CTL) means the concentration for each petroleum products’ contaminant of concern identified by an applicable analytical test method, in the medium of concern, at which a site rehabilitation program is deemed complete.

(8) “Contaminant” means any physical, chemical, biological, or radiological substance present in any medium that may result in adverse effects to human health or the environment, or that creates an adverse nuisance, organoleptic, or aesthetic condition in groundwater.

(9) “Contaminated” or “contamination” means the presence of petroleum or petroleum products or their chemical constituents in surface water, groundwater, soil, sediment, or upon the land, in concentrations that exceed the applicable CTLs specified in Chapter 62-777, F.A.C., or water quality standards in Chapter 62-302 or 62-520, F.A.C., or in concentrations that may result in contaminated sediment. This definition is solely for use within Chapter 62-770, F.A.C.

(10) “Contaminated sediment” means sediment that is contaminated with petroleum or petroleum products or their chemical constituents as determined by the concentrations of the petroleum or petroleum products’ contaminants of concern, actual circumstances of exposure, biological diversity studies, toxicity testing, or other evidence of harmful effects, as applicable. [Refer to the sediment guidelines referenced in subsection 62-770.140(2), F.A.C. for guidance on the evaluation of concentrations of petroleum products’ contaminants of concern, sediment quality conditions, and testing methods.]

(11) “Contamination” refer to the definition for “contaminated.”

(12) “CTL” means cleanup target level.

(13) “Department” means the Florida Department of Environmental Protection.

(14) “Discharge” includes, but is not limited to, any spilling, leaking, seeping, misapplying, pouring, emitting, emptying, releasing, or dumping of any petroleum or petroleum products, that occurs and that affects lands and the surface waters and ground waters of the State not regulated by Sections 376.011-.21, F.S.

(15) “Discharger” means the person who has dominion or control over the petroleum or petroleum products at the time of the discharge into the environment.

(16) “Discovery” means:

(a) Observance or detection of free product in boreholes, wells, open drainage ditches, open excavations or trenches, or on nearby surface water, or petroleum or petroleum products in excess of 0.01 foot in thickness in sewer lines, subsurface utility conduits or vaults, unless the product has been removed and it was confirmed that a release into the environment did not occur;

(b) Observance of visually stained soil or odor of petroleum products resulting from a discharge of used oil equal to, or exceeding, 25 gallons on a pervious surface [see paragraph 62-770.160(1)(c), F.A.C., for cleanup requirements applicable to discharges of less than 25 gallons];

(c) Discharges of petroleum or petroleum products equal to, or exceeding, 25 gallons on a pervious surface [see paragraph 62-770.160(1)(c), F.A.C., for cleanup requirements applicable to discharges of less than 25 gallons];

(d) Results of analytical test on a groundwater sample that exceed the CTLs referenced in Chapter 62-777, F.A.C., Table I, groundwater criteria column for the petroleum products’ contaminants of concern listed in Table A of this chapter; or

(e) Results of analytical test on a soil sample that exceed the lower of the direct exposure residential CTLs and leachability based on groundwater criteria CTLs specified in Chapter 62-777, F.A.C., Table II for the petroleum products’ contaminants of concern listed in Table A of this chapter.

(17) “Domestic purposes” means that the water is used for human consumption such as bathing, cooking, or drinking, and is provided through pipes or other constructed conveyances.

(18) “Engineering control” means use of existing features (such as buildings) or modifications to a site to reduce or eliminate the potential for migration of, or exposure to, petroleum products’ contaminants of concern. Examples of modifications include physical or hydraulic control measures, capping, point-of-use treatments, or slurry walls.

(19) “Excessively contaminated soil” for the purposes of Section 376.3071(11)(b)2., F.S., that only applies to sites scored 10 or less (unless laboratory results verify that the organic vapor analysis data are not relevant), means soil saturated with petroleum or petroleum products or soil that causes a total corrected hydrocarbon measurement of 500 parts per million (ppm) or higher for Gasoline Analytical Group or 50 ppm or higher for Kerosene Analytical Group. Readings shall be obtained at the site on an organic vapor analysis instrument with a flame ionization detector in the survey mode upon sampling the headspace in half-filled, 8-ounce or 16-ounce jars. Each soil sample shall be split into two jars, the two sub-samples shall be brought to a temperature of between 20° C. (68° F.) and 32° C. (90° F.), and the readings shall be obtained 5 to 30 minutes thereafter. One of the readings shall be obtained with the use of an activated charcoal filter unless the unfiltered reading is non-detect. The total corrected hydrocarbon measurement shall be determined by subtracting the filtered reading from the unfiltered reading. Instruments with a photo ionization detector may be used, but shall not be used in situations where humidity will interfere with the instruments’ sensitivity (including periods of rain, measuring wet or moist soil). If an instrument with a photo ionization detector is used, a filtered reading is not warranted and therefore sample splitting is not necessary. Analytical instruments shall be calibrated in accordance with the manufacturer’s instructions.

(20) “Exposure unit” means an area over which receptors are expected to have equal and random exposure.

(21) “FDEP” means the Florida Department of Environmental Protection.

(22) “FDEP local program” means a county or Department of Health local program established pursuant to a contract pursuant to Section 376.3073, F.S., to assist the Department in the administration of the petroleum contamination site cleanup.

(23) “Free product” means petroleum or petroleum product in excess of 0.01 foot in thickness, measured at its thickest point, floating on surface water or groundwater.

(24) “Gasoline Analytical Group” means aviation gasoline, gasohol, and motor gasoline or equivalent petroleum products.

(25) “Groundwater” means water beneath the surface of the ground within a zone of saturation, whether or not flowing through known or definite channels.

(26) “Innovative technology” means a process that has been tested and used as a treatment for contamination, but lacks an established history of full-scale use and information about its cost and how well it works sufficient to support prediction of its performance under a variety of operating conditions. An innovative technology is one that is undergoing pilot-scale treatability studies, that usually are performed in the field or the laboratory and require installation of the technology, and that provide performance, cost, and design objectives for the technology prior to full-scale use.

(27) “Institutional control” means a restriction on use of, or access to, a site to eliminate or minimize exposure to petroleum products’ contaminants of concern. Examples of institutional controls include deed restrictions, restrictive covenants, and conservation easements.

(28) “Interim source removal” means the removal of free product, contaminated groundwater, or contaminated soil, or the removal of contaminants from soil that has been contaminated to the extent that leaching to groundwater has occurred or is occurring, prior to approval of a Remedial Action Plan pursuant to Rule 62-770.700, F.A.C.

(29) “Kerosene Analytical Group” means diesel, Jet-A, Jet-B, JP-4, JP-5, and kerosene or equivalent petroleum products.

(30) “Low yield” means groundwater that is contained in an aquifer that has an average hydraulic conductivity of less than one foot per day, determined by performing slug tests or an equivalent method for determining hydraulic conductivity on a minimum of three monitoring wells in each affected monitoring zone; and a maximum yield of 80 gallons per day, determined by pumping a four inch well screened across the cross-section of the plume, for a minimum of two hours.

(31) “Monitoring well” means a well constructed with a surface seal and a sand filter pack in accordance with accepted design practices in order to provide for the collection of representative groundwater samples for laboratory analyses. Such wells may also be used to detect the presence of free product or collect water-level elevation data to aid in determining the direction of groundwater flow.

(32) “MTBE” means Methyl tert-butyl ether.

(33) “Natural attenuation” means a verifiable approach to site rehabilitation that allows natural processes to contain the spread of contamination and reduce the concentrations of petroleum products’ contaminants of concern in contaminated groundwater and soil. Natural attenuation processes may include sorption, biodegradation, chemical reactions with subsurface materials, diffusion, dispersion, and volatilization.

(34) “Newspaper of general circulation” means a newspaper published at least on a weekly basis and printed in the language most commonly spoken in the area within which it circulates, but does not include a newspaper intended primarily for members of a particular professional or occupational group, a newspaper whose primary function is to carry legal notices, or a newspaper that is given away primarily to distribute advertising.

(35) “Organoleptic” means pertaining to, or perceived by, a sensory organ (i.e., color, taste, or odor).

(36) “PAHs” means Polycyclic Aromatic Hydrocarbons.

(37) “PCBs” means Polychlorinated Biphenyls.

(38) “Person responsible for site rehabilitation” (PRSR) means the real property owner, the facility owner, the facility operator, the discharger, or other person or entity responsible for site rehabilitation, or the Department when the Department is conducting the site rehabilitation at facilities with discharges eligible for State-funded cleanup pursuant to Sections 376.305(6), 376.3071(9), 376.3071(13), and 376.3072, F.S.

(39) “Petroleum contamination site” means any contiguous land, sediment, surface water, or groundwater area upon or into which a discharge of petroleum or petroleum products has occurred or for which evidence exists that such a discharge has occurred.

(40) “Petroleum products’ contaminants of concern” means the contaminants listed in Table A of this chapter and similar chemicals found in additives, provided the contaminants are present as a result of a discharge of petroleum or petroleum products.

(41) “Piezometer” means a permanent or temporary well that may be designed and constructed without the surface sealing or sand filter pack requirements of a monitoring well. This type of well is primarily used to detect the presence of free product or collect water-level elevation data to aid in determining the direction of groundwater flow.

(42) “Plume” means the portion of an aquifer or aquifers in which groundwater contamination by petroleum products’ contaminants of concern above applicable CTLs, and background concentrations as defined in subsection 62-770.200(5), F.A.C., has been detected.

(43) “Poor quality” means groundwater within the affected monitoring zone with background concentrations, as defined in subsection 62-770.200(5), F.A.C., that exceed any of Florida’s Primary or Secondary Drinking Water Standards referenced in Chapter 62-550, F.A.C.

(44) “Practical quantitation limit” (PQL) means the lowest level that can be reliably measured during routine laboratory operating conditions within specified limits of precision and accuracy. [Refer to the PQL guidelines referenced in subsection 62-770.140(5), F.A.C., for guidance.]

(45) “Priority pollutant” means any compound listed in 40 CFR Part 122, Appendix D, Tables II through IV.

(46) “Product recovery” means the removal of free product.

(47) “PRSR” means person responsible for site rehabilitation.

(48) “Real property owner” means the person or entity that is vested with ownership, dominion, or legal or rightful title to the real property.

(49) “Reportable quantity” means a discharge of petroleum or petroleum products equal to, or exceeding, 25 gallons on a pervious surface.

(50) “Responsible party” means the real property owner, the facility owner, the facility operator, or the discharger, or other person or entity responsible for site rehabilitation unless that entity is the Department.

(51) “Sediment” means the unconsolidated solid matrix occurring immediately beneath any surface water body. The surface water body may be present part or all of the time and may support a wetland environment or vegetation.

(52) “Site” refer to the definition for “petroleum contamination site.”

(53) “Site assessment” means the performance of any of the tasks or activities as described in Rules 62-770.300 and 62-770.600, F.A.C.

(54) “Site rehabilitation” means the assessment of site contamination and the remediation activities that reduce the levels of contaminants of concern at a site through accepted treatment methods to meet the CTLs established for that site.

(55) “Soil saturated with petroleum or petroleum products” means soil observed to contain petroleum or petroleum products that drain from the soil when it is handled or squeezed, or create streaks of petroleum or petroleum products on excavation tools or on plastic sheeting upon exposure to the soil.

(56) “Source removal” means the removal of free product, contaminated groundwater, or contaminated soil, or the removal of contaminants from soil that has been contaminated to the extent that leaching to groundwater has occurred or is occurring, after approval of a Remedial Action Plan pursuant to Rule 62-770.700, F.A.C.

(57) “Surface water” means water upon the surface of the earth, whether contained in bounds created naturally or artificially or diffused. Water from natural springs shall be classified as surface water when it exits from the spring onto the earth’s surface.

(58) “Synergistic effect” means a scientific principle that the toxicity that occurs as a result of exposure is more than the sum of the toxicities of the individual chemicals to which an individual is exposed.

(59) “Temporary point of compliance” (TPOC) is the boundary represented by one or more designated monitoring wells at which groundwater CTLs may not be exceeded while site rehabilitation is proceeding.

(60) “Total Volatile Organic Aromatics” means the sum of concentrations of Benzene, Toluene, total Xylenes, and Ethylbenzene.

(61) “TPOC” means temporary point of compliance.

(62) “TRPHs” means Total Recoverable Petroleum Hydrocarbons.

(63) “UCL” means upper confidence limit estimate of the arithmetic mean.

(64) “Used oil” means any lubricants for use in internal combustion engines that have been refined from crude oil and, as a result of use, storage, or handling, have become unsuitable for their original purpose due to the presence of impurities or loss of properties, but that may be suitable for further use as a fuel or are economically recyclable for use as a fuel. “Used oil” shall not include any used oil that has been mixed with any material that is a hazardous waste, unless the material is a hazardous waste solely due to the characteristic of ignitability as defined in 40 CFR Part 261, Subpart C.

(65) “VOHs” means Volatile Organic Halocarbons.

(66) “Waters” or “waters of the State” means waters as defined in Section 403.031, F.S.

Specific Authority 376.303, 376.3071 FS. Law Implemented 376.3071 FS. History–New 11-1-87, Formerly 17-70.003, Amended 2-21-90, Formerly 17-770.200, Amended 9-23-97, 8-5-99, 4-17-05.