64E-8.004 Limited Use System Operating Permits.

(1) Annual permits are required for all limited use systems, except those systems registered per subsection 64E-8.004(6), F.A.C. Annual operating permits expire September 30.

(2) By September 1st each year, the owner of a non-registered Limited Use System shall submit the following items to the county health department:

(a) A completed Form DH 4092A, 9/97, for a new water system or a water system modified since the previous permit was issued;

(b) A $75 operating permit application fee the first year, and then a $70 annual operating permit fee each year thereafter. The initial operating permit fee for a system put into operation after March 31st is $35;

(c) Limited use commercial water systems which serve family day care establishments as described in Chapter 65C-20, F.A.C., shall pay an annual operating permit fee of $25. The initial operating permit fee for a family day care establishment’s water system put into operation after March 31st is $15;

(d) For the initial permit, evidence that the water meets paragraph 64E-8.006(1)(a), F.A.C., chemical MCL’s and a recent, satisfactory two consecutive day source water microbiological survey;

(e) For the initial permit, a minimum size 8.5 × 11 inch site plan of sufficient clarity to be reproduced;

(f) For the initial permit, the capacity/size, model, and brand of all system components; and

(g) A well completion report the first year, if available, and then any time a well is replaced.

(3) Upon receipt of satisfactory items in subsection 64E-8.004(2), F.A.C., and a satisfactory sanitary survey, the department shall issue authorization on Form DH 4093 to operate the system.

(4) A satisfactory sanitary survey conducted by the department in the last twelve months shall assure that:

(a) Setbacks in Rule 64E-8.002, F.A.C. are met, except that system supplied by a well constructed prior to January 1, 1993 that is between 50 and 100 feet from an OSTDS shall be permitted without a variance if:

1. The well was constructed and approved as a potable water well;

2. Both the well and the OSTDS were permitted and approved at the time of construction for the proposed and existing use, and the OSTDS is otherwise in compliance with Rule Chapter 64E-6, F.A.C.;

(b) The pressure is twenty pounds per square inch throughout the system at all times;

(c) The system contains no cross connections;

(d) A finished water microbiological sample (and if disinfected, a source water sample) is collected by department staff, for no additional fee;

(e) A raw water source tap complying with paragraph 64E-8.002(3)(a), F.A.C., is provided;

(f) All chemically disinfected systems shall have an aboveground check valve between the raw water source tap and the disinfectant injection point;

(g) All systems which are required to be chemically disinfected maintain a minimum 15 minute disinfectant contact time at peak demand flow;

(h) The system or system use has not been modified without prior approval by the department.

(5) Mandated corrective actions must be completed within 120 days of permit denial.

(6) Suppliers of Limited Use Commercial Public Water Systems that do not make tap water available for public consumption are exempt from obtaining annual operating permits, provided they have

(a) Registered the system by submitting a $15 registration fee and a completed registration application Form DH 4095 to the county health department,

(b) Performed a satisfactory, two-consecutive-day, coliform bacteria analysis of the source water. The department shall waive this requirement upon conversion from a permitted to a registered system if all untreated distribution sample analyses have been satisfactory for the previous calendar year,

(c) Performed within the last five years,

1. A satisfactory nitrate analysis of water representative of the source and any satisfactory analysis required per paragraph 64E-8.006(2)(d), F.A.C., and

2. A satisfactory lead analysis of first-flush, indoor tap water which has been undisturbed in the plumbing for at least six hours,

(d) Performed one satisfactory, coliform bacteria analysis of water from the distribution system, and

(e) Provided satisfactory analyses reports as required in this section within 60 days of notification by the department.

(f) Re-registration, including a $15 fee and monitoring, shall be required prior to changing business activity and upon changing system ownership.

(g) In order to retain their potable water status as is required by the Federal Occupational Health and Safety Administration Rule 29 CFR 1910.141, and the Florida Plumbing Code, limited use commercial registered systems as described within this paragraph must, conduct annual testing for bacteria in the form of one satisfactory microbiological sample per calendar year.

(h) Upon receipt of satisfactory items in rule (a) through (f) above, the department shall issue authorization to operate the registered system.

Specific Authority 403.862(1)(f), 381.0011(4), (13), 381.006, 381.0062(1), (3)(a), (6) FS. Law Implemented 381.0012, 381.006(1), (2), 381.0061, 381.0062, 381.0067, 403.862(1)(f) FS. History–New 1-1-93, Amended 8-20-96, Formerly 10D-4.027, Amended 1-26-98, 1-24-00, 11-13-00, 10-7-02.