68D-18.004 Special Purpose Marker Buoys.

(1) In order that special purpose marker buoys shall not be mistaken for aids to navigation or regulatory markers, they shall be of cylindrical shape of white with 6 inch international orange rings spaced 6 inches apart over the entire length of the buoy. Surface of buoy must extend a minimum of 48 inches above the water line.

(2) These markers are to be used by the Fish and Wildlife conservation Commission and other organizations to mark or outline areas for special marine events.

(3) Request for these buoys will be processed in the same manner as waterway markers.

(4) Organizations to which the special purpose markers are authorized will assume the responsibility for their placement, removal, maintenance and proper storage.

(5) These buoys will not be permanently positioned in the water and may not be left in position.

Rulemaking Authority 327.04, 327.40, 327.41 FS. Law Implemented 327.40, 327.41 FS., ch. 72-55, Laws of Florida. History–New 10-20-72, Readopted 9-30-75, Formerly 16B-18.04, 16N-18.04, 16N-18.004, 62N-18.004.