## 69A-51.045 Scope.

(1) The provisions of this part shall apply to existing and new installations of boilers in public assembly locations.

(2) Existing installations are those boilers installed in public assembly locations before October 1, 1987.

(3) For existing installations:

(a) The maximum allowable working pressure of a boiler carrying the ASME Code symbol stamp shall be determined by the applicable sections of the ASME Code under which it was constructed and stamped.

(b) The maximum allowable working pressure of a boiler which does not carry the ASME Code symbol shall be computed in accordance with the inspection code of the National Board of Boiler and Pressure Vessel Inspectors, as adopted and incorporated by reference herein.

(c) These rules shall not be construed to prevent the use, sale or reinstallation of a boiler in a public assembly location, provided it has been made to conform to the rules in this rule chapter governing existing installations and, provided further, that it has not been found upon inspection to be in an unsafe condition.

(4) New installations are those boilers installed in public assembly locations after September 30, 1987.

(5) For new installations, no boiler which does not conform to the rules in this rule chapter governing new construction and installation shall be installed and operated in public assembly locations in this state unless the boiler is of special design or construction, and is not inconsistent with the spirit and safety objectives of these rules in which case a permit for a state special must be applied for in writing by the Florida user. After specific approval, the issuance of a Florida State Special Number and a certificate of compliance may be granted at the discretion of the chief inspector of the Boiler Safety Program.

(6) No boiler shall be installed in a public assembly location in this state unless it has been constructed, inspected and stamped in conformity with the ASME Code, except:

(a) Those exempted by the Act; or

(b) Boilers which are federally owned and federally inspected; or

(c) Coil type hot water boilers without any steam space where water flashes into steam when released through a manually operated nozzle unless one of the following limitations is exceeded:

1. A 3/4'' inch diameter tubing or pipe size with no drum or headers attached; or

2. Nominal water containing capacity does not exceed six U.S. gallons; or

3. Water temperature does not exceed 350º F.; or

4. Steam is not generated within the coil; or

(d) Those potable water heaters exempted by Part HLW-101, “Service Restriction and Exception,” Section IV of the ASME Code; or

(e) Those approved as a Florida State Special.

Rulemaking Authority 554.103 FS. Law Implemented 554.103, 554.104, 554.105, 554.106, 554.107, 554.108, 554.109, 554.1101 FS. History–New 2-27-89, Formerly 4A-51.045.