62-18.520  Instrumentation.

Equipment used in making vehicle sound measurements shall meet the following requirements:

(1) Sound Level Meter. Sound level meters shall be of the precision type meeting A-weighting requirements and specifications of the American National Standards Institute, Inc., or its successor bodies. Alternately, a microphone/magnetic tape recorder/indicating meter system whose overall response is equivalent to the above may be used.

(2) Sound Level Calibrator. The sound level calibrator shall calibrate the entire sound level meter with an acoustic calibrator of the coupler type, following the manufacturer’s recommended procedures.

(3) Tachometer. A calibrated engine speed tachometer shall be used to determine maximum rated rpm.

(4) Anemometer. An anemometer shall be used to measure the wind speed at the test site.

(5) Windscreen. A properly installed windscreen recommended by the manufacturer of the sound level meter may be used.

Rulemaking Authority 403.061 FS. Law Implemented 403.061, 403.415(5) FS., Chapter 74-110, Laws of Florida. History–New 11-27-74, Formerly 17-18.52, 17-18.520.