## 40D-3.600 Special Well Construction Standards.

To prevent impacts to water wells from periodic high water use, in addition to complying with the other construction requirements of this chapter, the construction, modification or repair of potable water wells in the area of the Dover community shall also comply with the requirements set forth below.

(1) Potable water wells constructed, modified or repaired in the North Dover Area, as identified in subsection (2), below, shall be cased to a minimum depth of 105 feet below land surface.

(2) The area of North Dover is as follows:

Township 27, Range 21, Sections 25 through 36;

Township 27, Range 22, Sections 26 through 35;

Township 28, Range 20, Sections 12 through 14, 23, 24 and those portions of 25 and 26 lying north of Interstate 4;

Township 28, Range 21, Sections 1 through 19 and those portions of 20 through 24 and 30 lying north of Interstate 4; and

Township 28, Range 22, Sections 2 through 10, 15 through 20, Sections 22 through 27, and Sections 34 through 36.

(3) Potable water wells constructed, modified or repaired in the South Dover Area, as identified in subsection (4), below, shall be cased to a minimum depth of 147 feet below land surface.

(4) The area of South Dover is as follows:

Township 28, Range 20, those portions of Sections 25 and 26 lying south of Interstate 4 and Sections 35 and 36;

Township 28, Range 21, those portions of Sections 20 through 24 and 30 lying south of Interstate 4 and Sections 25 through 29 and 31 through 36;

Township 29, Range 20, Sections 1, 2, 11 through 13 and 24;

Township 29, Range 21, Sections 1 through 29, and 33 through 36;

Township 29, Range 22, Sections 1 through 36;

Township 30, Range 21, Sections 1, 2, 11, and 12; and

Township 30, Range 22, Sections 2 through 10.

Rulemaking Authority 373.044, 373.113, 373.171, 373.308 FS. Law Implemented 373.308, 373.309 FS. History–New 4-9-02, Amended 8-17-10.