62-306.500 Credit Generation and Validation.

(1) Point Sources.

(a) The baseline for point sources, including both wastewater and stormwater dischargers, shall be the source’s wasteload allocation under the LSJR BMAP, unless a lower water quality-based effluent limitation has been established for the discharge.

(b) Credits shall only be generated by point sources after the entity provides reasonable assurance that it can meet an effluent loading limit that is lower than its baseline allocation and the source’s applicable permit limits are revised to reflect the reduced load.

(2) Nonpoint Sources.

(a) The baseline for nonpoint sources shall be the source’s load allocation specified under the LSJR BMAP or, for nonpoint sources that are covered under categorical load allocations, shall be the load expected following implementation of applicable BMPs and the additional reductions required for agricultural sources.

(b) Credits shall only be generated by nonpoint sources if the source reaches an agreement with a permitted point source and the activity generating the credits is incorporated into the point source’s permit.

Rulemaking Authority 403.067(9) FS. Law Implemented 403.067(8)-(10) FS. History–New 9-6-10.