## 62-610.652 Waste Treatment, Disinfection, and Monitoring.

(1) Preapplication waste treatment shall result in a reclaimed water that meets secondary treatment and basic disinfection. If required by subsection 62-610.652(5), F.A.C., additional treatment and disinfection shall be provided.

(2) Individual industrial activities or users may have water quality needs which may necessitate treatment beyond the minimum requirements established in this part. The Department shall not regulate these additional treatment and disinfection requirements. These additional treatment and disinfection requirements shall be subject to negotiation between the industry and the supplier of the reclaimed water.

(3) Except as provided in paragraph 62-610.668(2)(d), F.A.C., domestic wastewater treatment or disinfection provided at the industrial facility before reuse of the reclaimed water at the industrial facility shall be subject to domestic wastewater permitting if the treatment or disinfection at the industrial site is needed to meet the minimum treatment and disinfection requirements imposed by this part of Chapter 62-610, F.A.C.

(4) If additional treatment or disinfection is provided at the industrial facility before reuse of the reclaimed water at the industrial facility, and the additional treatment or disinfection is provided only to meet water quality needs of the industry which are more stringent than the minimum requirements imposed by this part, domestic wastewater permitting shall not be needed for the additional treatment or disinfection facilities located at the industrial facility.

(5) All requirements of Part III of Chapter 62-610, F.A.C., including minimum system size requirements, shall be met if reclaimed water will be used in open cooling tower applications, except as provided in paragraph 62-610.668(2)(c) or (d), F.A.C.

(6) Monitoring.

(a) Waste treatment limitations shall be met after disinfection and before discharge to system storage or the reuse system.

(b) If high-level disinfection is provided, the total suspended solids limitation shall be met after filtration and before application of the disinfectant.

(c) For facilities that provide reclaimed water for use in open cooling towers, the permittee shall sample the reclaimed water for Cryptosporidium and Giardia. The following requirements shall be met:

1. Sampling shall be conducted at one time during each two-year period. Intervals between sampling shall not exceed two years. This sampling frequency is independent of the treatment plant’s capacity.

2. Samples shall be taken from at a point immediately following the disinfection process.

Rulemaking Authority 403.051, 403.061, 403.087 FS. Law Implemented 403.021, 403.051, 403.061, 403.062, 403.085, 403.086, 403.087, 403.088 FS. History–New 1-9-96, Amended 8-8-99.