## 64E-5.1421 Inspection and Maintenance.

(1) The licensee shall perform inspection and maintenance checks that include, as a minimum, each of the following at the frequency specified in the license or license application:

(a) Operation of each aspect of the access control system required by Rule 64E-5.1406, F.A.C.;

(b) Functioning of the source position indicator required by subsection 64E-5.1410(2), F.A.C.;

(c) Operation of the radiation monitor on the pool water purification system using a radioactive check source to detect radioactive contamination in pool water as required by subsection 64E-5.1409(2), F.A.C.;

(d) Operation of the over-pool radiation monitor at underwater irradiators as required by subsection 64E-5.1409(3), F.A.C.;

(e) Operation of the product exit monitor required by subsection 64E-5.1409(1), F.A.C.;

(f) Operation of the emergency source return control required by subsection 64E-5.1410(3), F.A.C.;

(g) Leak-tightness of systems through which pool water circulates (visual inspection);

(h) Operation of the heat and smoke detectors and extinguisher system required by Rule 64E-5.1408, F.A.C., but without turning on extinguishers;

(i) Operation of the means of pool water replenishment required by subsection 64E-5.1411(3), F.A.C.;

(j) Operation of the visible indicator of low and high pool water level required by subsection 64E-5.1411(4), F.A.C.;

(k) Operation of the intrusion alarm required by subsection 64E-5.1406(2), F.A.C.;

(l) Functioning and wear on the system, mechanisms, and cables used to raise and lower sources;

(m) Condition of the barrier to prevent products from hitting the sources or source mechanism and the operation of the collision alarm system, as required by Rule 64E-5.1412, F.A.C.;

(n) Amount of water added to the pool to determine if the pool is leaking;

(o) Electrical wiring on required safety systems for radiation damage;

(p) Pool water conductivity measurements and analysis as required by Rule 64E-5.1422, F.A.C.;

(q) Condition of the product carriers; and,

(r) Operation of the siphon breakers in the pool plumbing.

(2) Malfunction and defects found during inspection and maintenance checks must be repaired without undue delay.

Rulemaking Authority 404.051(4) FS. Law Implemented 404.051(1), (5), (6), 404.061, 404.081, 404.141 FS. History–New 8-14-96, Formerly 10D-91.1521.