Title	40—Protection	of

Environment

(This book contains parts 136 to 149)

Part

## CHAPTER I—Environmental Protection Agency (Continued)	136

CHAPTER I—ENVIRONMENTAL PROTECTION AGENCY (CONTINUED)

EDITORIAL  NOTE:  Nomenclature  changes  to  chapter  I  appear  at  65  FR  47324,  47325,  Aug.  2, 2000, and at 66 FR 34375, 34376, June 28, 2001.

SUBCHAPTER D—WATER PROGRAMS (CONTINUED)

| Part 136 | Guidelines establishing test procedures for the | Page |
| --- | --- | --- |
|  | analysis of pollutants ........................................... | 5 |
| 140 | Marine sanitation device standard .......................... | 377 |
| 141 | National primary drinking water regulations ........ | 381 |
| 142 | National primary drinking water regulations im- |  |
|  | plementation ........................................................ | 691 |
| 143 | National secondary drinking water regulations ..... | 751 |
| 144 | Underground injection control program ................. | 756 |
| 145 | State UIC program requirements ............................ | 825 |
| 146 | Underground injection control program: Criteria |  |
|  | and standards ....................................................... | 838 |
| 147 | State, tribal, and EPA-administered underground |  |
|  | injection control programs .................................. | 891 |
| 148 | Hazardous waste injection restrictions ................... | 996 |
| 149 | Sole source aquifers ................................................ | 1005 |

SUBCHAPTER D—WATER PROGRAMS (CONTINUED)

# PART 136—GUIDELINES ESTAB- LISHING TEST PROCEDURES FOR THE ANALYSIS OF POLLUTANTS

Sec.

  - Applicability.

  - Definitions.

  - Identification of test procedures.

  - Application for and approval of alter- nate  test  procedures  for  nationwide  use.

  - Approval of alternate test procedures for limited use.

  - Method modifications and analytical requirements.

  - Quality assurance and quality control. APPENDIX A TO PART 136—METHODS FOR OR-

GANIC  CHEMICAL  ANALYSIS  OF  MUNICIPAL

AND INDUSTRIAL WASTEWATER

APPENDIX B TO PART 136—DEFINITION AND PROCEDURE  FOR  THE  DETERMINATION   OF THE METHOD DETECTION LIMIT—REVISION 1.11

APPENDIX C TO PART 136—DETERMINATION OF METALS AND TRACE ELEMENTS  IN  WATER AND WASTES BY INDUCTIVELY COUPLED PLASMA-ATOMIC EMISSION SPECTROMETRY METHOD 200.7

APPENDIX D TO PART 136—PRECISION AND RE- COVERY STATEMENTS FOR METHODS FOR MEASURING METALS

AUTHORITY: Secs. 301, 304(h), 307 and 501(a), Pub. L. 95–217, 91 Stat. 1566, et seq. (33 U.S.C.

1251, et seq.) (the Federal Water Pollution Control Act Amendments of 1972 as amended by the Clean Water Act of 1977).

##### § 136.1   Applicability.

- The procedures prescribed herein shall, except as noted in §§ 136.4, 136.5, and 136.6, be used to perform the meas- urements indicated whenever the waste constituent specified is required to be measured  for:

  - An application submitted to the Administrator, or to a State having an approved NPDES program for a permit under section 402 of the Clean Water Act of 1977, as amended (CWA), and/or to reports required to be submitted under NPDES permits  or  other  re- quests for quantitative or qualitative effluent data under parts 122 to 125 of title 40; and

  - Reports required  to be submitted by dischargers under the NPDES estab- lished by parts 124 and 125 of this chap- ter; and

  - Certifications issued by States pursuant to section 401 of the CWA, as amended.

- The procedure prescribed herein and in part 503 of title 40 shall be used to perform the measurements required for an application submitted to the Ad- ministrator or to a State for a sewage sludge permit  under  section  405(f)  of the Clean Water Act and for record- keeping and reporting requirements under part 503 of title 40.

- For the purposes of the NPDES program, when more than one  test pro- cedure is approved under this part for the analysis of a pollutant or pollutant parameter, the test procedure must be sufficiently sensitive as  defined  at  40 CFR 122.21(e)(3) and 122.44(i)(1)(iv).

[72 FR 14224, Mar. 26, 2007, as amended at 77

FR 29771,  May 18,  2012;  79  FR 49013,  Aug. 19,

2014]

##### § 136.2   Definitions.

As used in this part, the term:

- Act means the Clean Water Act of 1977, Pub. L. 95–217, 91 Stat. 1566, et seq. (33 U.S.C. 1251 et seq.) (The Federal Water Pollution Control Act Amend- ments of 1972 as amended by the Clean Water Act of 1977).

- Administrator means the Adminis- trator of the U.S. Environmental Pro- tection Agency.

- Regional Administrator means one of the EPA Regional Administrators.

- Director means the Director of the State Agency authorized to carry  out an approved National Pollutant Dis- charge Elimination System Program under section 402 of the Act.

- National Pollutant Discharge Elimi- nation System (NPDES) means the na- tional system for the issuance of per- mits under section  402 of  the Act and includes any State or interstate pro- gram which has been approved by the Administrator, in whole or in part, pursuant to section 402 of the Act.

- Detection limit means the minimum concentration of an analyte (sub- stance) that can be measured and re- ported with a 99% confidence that the analyte  concentration  is  greater  than

§ 136.3

zero  as  determined  by  the  procedure set forth at appendix B of this part.

[38 FR 28758, Oct. 16, 1973, as amended at 49

FR 43250, Oct. 26, 1984]

##### § 136.3   Identification   of   test   proce- dures.

  - Parameters or pollutants,  for which methods are approved, are listed together with test procedure descrip- tions and references in Tables IA,  IB, IC, ID, IE, IF, IG, and IH. The methods listed in Tables IA, IB, IC,  ID,  IE,  IF, IG, and IH are incorporated by ref- erence, see paragraph (b) of this sec- tion, with the exception of EPA  Meth- ods 200.7, 601–613, 624, 625, 1613, 1624, and 1625. The full texts of Methods 601–613, 624, 625, 1613, 1624, and 1625 are printed in appendix A of this part  136,  and  the full text of Method 200.7 is printed in appendix C of this part 136. The full text for determining the method detec- tion limit when using the test proce- dures  is  given  in  appendix  B  of  this part 136. The full text of Method 200.7 is

#### 40 CFR Ch. I (7–1–17 Edition)

printed in appendix C  of  this  part  136. In the event of a conflict between the reporting  requirements  of  40  CFR  parts

122 and 125 and any reporting require- ments associated with the methods listed in these tables, the provisions of 40 CFR parts 122 and 125 are controlling and will determine a permittee’s re- porting requirements. The full text of the referenced test procedures are in- corporated by reference into Tables IA, IB, IC,  ID,  IE, IF,  IG,  and  IH. The  dis- charge parameter values for which re- ports are required must be determined by one of the standard analytical test procedures incorporated by reference and described in Tables IA, IB, IC, ID, IE, IF, IG, and IH or by any alternate test procedure which has been approved by the Administrator under the provi- sions of paragraph (d) of this section and §§ 136.4 and 136.5. Under certain cir- cumstances paragraph (c) of this sec- tion, § 136.5(a) through (d) or 40 CFR 401.13, other additional or alternate test procedures may be used.

TABLE IA—LIST OF APPROVED BIOLOGICAL METHODS FOR WASTEWATER AND SEWAGE SLUDGE

| Parameter and units | Method 1 | EPA | Standard methods | AOAC, ASTM, USGS | Other |
| --- | --- | --- | --- | --- | --- |
| Bacteria: Coliform (fecal), num- ber per 100 mL or num- ber per gram dry weight. Coliform (fecal) in presence of chlorine, number per 100 mL. Coliform (total), num- ber per 100 mL. Coliform (total), in presence of chlorine, number per 100 mL. E. coli, number per 100 mL 21. | Most Probable Number (MPN), 5 tube, 3 dilu- tion, or Membrane filter (MF) 2, single step MPN, 5 tube, 3 di- lution, or MF 2, single step 5 MPN, 5 tube, 3 di- lution, or. MF 2, single step or two step. MPN, 5 tube, 3 di- lution, or MF 2 with enrich- ment 5. MPN 6 8 16 multiple tube, or. multiple tube/mul- tiple well, or | p. 132 3 ................ 1680. 11 15 1681 11 20 p. 124 3 ................ p. 132 3 ................ p. 124 3 ................ p. 114 3 ................ p. 108 3 ................ p. 114 3 ................ p. 111 3 ................ .............................. .............................. | 9221 C E–2006. 9222 D–1997 ....... 9221 C E–2006. 9222 D–1997. 9221 B–2006. 9222 B–1997 ....... 9221 B–2006 9222 (B + B.5c) ¥ 1997. 9221B.1–2006/ 9221F– 2006 12 14. 9223 B–200 413 ... | B–0050–85 4. B–0025–85 4 991.15 10 .................... | Colilert 13 18 Colilert-1813 17 18 |

#### Environmental Protection Agency	§ 136.3

TABLE IA—LIST OF APPROVED BIOLOGICAL METHODS FOR WASTEWATER AND SEWAGE SLUDGE—

Continued

| Parameter and units | Method 1 | EPA | Standard methods | AOAC, ASTM, USGS | Other |
| --- | --- | --- | --- | --- | --- |
| Fecal streptococci, number per 100 mL. Enterococci, number per 100 mL 22. Salmonella, number per gram dry weight 11. Aquatic Toxicity: Toxicity, acute, fresh water orga- nisms, LC50, percent efflu- ent. Toxicity, acute, estua- rine and ma- rine orga- nisms of the Atlantic Ocean and Gulf of Mex- ico, LC50, percent efflu- ent. | MF 2 6 7 8 single step. MPN, 5 tube 3 di- lution, or MF 2, or ................ Plate count .......... MPN 6 8, multiple tube/multiple well, or MF 2 6 7 8 single step or. Plate count .......... MPN multiple tube Ceriodaphnia dubia acute. Daphnia puplex and Daphnia magna acute. Fathead Minnow, Pimephales promelas, and Bannerfin shin- er, Cyprinella leedsi, acute. Rainbow Trout, Oncorhynchus mykiss, and brook trout, Salvelinus fontinalis, acute. Mysid, Mysidopsis bahia, acute. Sheepshead Min- now, Cyprinodon variegatus, acute. Silverside, Menidia beryllina, Menidia menidia, and Menidia peninsulae, acute. | 1603 22 ................. p. 139 3 ................ p. 136 3 ................ p. 143 3 .............................. 1600 25 ................. p. 143 3 1682 23 2002.0.26 2021.0.26 2000.0.26 2019.0.26 2007.0.26 2004.0 26 2006.0 26 | .............................. 9230 B–2007. 9230 C–2007 ....... .............................. 9230 C–2007 | .................................... B–0055–85 4 D6503–99 9 ................ | mColiBlue-24 19 Enterolert13 24 |

#### § 136.3

40 CFR Ch. I (7–1–17 Edition)

TABLE IA—LIST OF APPROVED BIOLOGICAL METHODS FOR WASTEWATER AND SEWAGE SLUDGE—

Continued

| Parameter and units | Method 1 | EPA | Standard methods | AOAC, ASTM, USGS | Other |
| --- | --- | --- | --- | --- | --- |
| Toxicity, chronic, fresh water organisms, NOEC or IC25, percent effluent. Toxicity, chronic, es- tuarine and marine orga- nisms of the Atlantic Ocean and Gulf of Mex- ico, NOEC or IC25, per- cent effluent. | Fathead minnow, Pimephales promelas, larval survival and growth. Fathead minnow, Pimephales promelas, em- bryo-larval sur- vival and teratogenicity. Daphnia, Ceriodaphnia dubia, survival and reproduc- tion. Green alga, Selenastrum capricornutum, growth. Sheepshead min- now, Cyprinodon variegatus, lar- val survival and growth. Sheepshead min- now, Cyprinodon variegatus, em- bryo-larval sur- vival and teratogenicity. Inland silverside, Menidia beryllina, larval survival and growth. Mysid, Mysidopsis bahia, survival, growth, and fe- cundity. Sea urchin, Arbacia punctulata, fer- tilization. | 1000.0.27 1001.0.27 1002.0.27 1003.0.27 1004.0.28 1005.0.28 1006.0.28 1007.0.28 1008.0.28 |  |  |  |

Table IA notes:

1 The method must be specified when results are reported.

2 A 0.45-m membrane filter (MF) or other pore size certified by the manufacturer to fully retain organisms to be cultivated and to be free of extractables which could interfere with their growth.

3 Microbiological Methods for Monitoring the Environment, Water, and Wastes, EPA/600/8–78/017. 1978. US EPA.

4 U.S. Geological Survey Techniques of Water-Resource Investigations, Book 5, Laboratory Analysis, Chapter A4, Methods for Collection and Analysis of Aquatic Biological and Microbiological Samples. 1989. USGS.

5 Because the MF technique usually yields low and variable recovery from chlorinated wastewaters, the Most Probable Number

method will be required to resolve any controversies.

6 Tests must be conducted to provide organism enumeration (density). Select the appropriate configuration of tubes/filtrations and dilutions/volumes to account for the quality, character, consistency, and anticipated organism density of the water sample.

7 When the MF method has been used previously to test waters with high turbidity, large numbers of noncoliform bacteria, or

samples that may contain organisms stressed by chlorine, a parallel test should be conducted with a multiple-tube technique to demonstrate applicability and comparability of results.

8 To assess the comparability of results obtained with individual methods, it is suggested that side-by-side tests be conducted

across seasons of the year with the water samples routinely tested in accordance with the most current Standard Methods for the Examination of Water and Wastewater or EPA alternate test procedure (ATP) guidelines.

9 Annual Book of ASTM Standards–Water and Environmental Technology, Section 11.02. 2000, 1999, 1996. ASTM Inter-

national.

#### Environmental Protection Agency	§ 136.3

10 Official Methods of Analysis of AOAC International. 16th Edition, 4th Revision, 1998. AOAC International.

11 Recommended for enumeration of target organism in sewage sludge.

12 The multiple-tube fermentation test is used in 9221B.1–2006. Lactose broth may be used in lieu of lauryl tryptose broth (LTB), if at least 25 parallel tests are conducted between this broth and LTB using the water samples normally tested, and this comparison demonstrates that the false-positive rate and false-negative rate for total coliform using lactose broth is less than 10 percent. No requirement exists to run the completed phase on 10 percent of all total coliform-positive tubes on a seasonal basis. 13 These tests are collectively known as defined enzyme substrate tests, where, for example, a substrate is used to detect the

enzyme b-glucuronidase produced by E. coli.

14 After prior enrichment in a presumptive medium for total coliform using 9221B.1–2006, all presumptive tubes or bottles showing any amount of gas, growth or acidity within 48 h 3 h of incubation shall be submitted to 9221F–2006. Commercially available EC–MUG media or EC media supplemented in the laboratory with 50 g/mL of MUG may be used.

15 Method 1680: Fecal Coliforms in Sewage Sludge (Biosolids) by Multiple-Tube Fermentation Using Lauryl-Tryptose Broth (LTB) and EC Medium, EPA–821–R–10–003. April 2010. U.S. EPA.

16 Samples shall be enumerated by the multiple-tube or multiple-well procedure. Using multiple-tube procedures, employ an appropriate tube and dilution configuration of the sample as needed and report the Most Probable Number (MPN). Samples test- ed with Colilertmay be enumerated with the multiple-well procedures, Quanti-Tray, Quanti-Tray/2000, and  the MPN cal- culated from the table provided by the manufacturer.

17 Colilert-18is an optimized formulation of the Colilertfor the determination of total coliforms and E. coli that provides re- sults within 18 h of incubation at 35 C rather than the 24 h required for the Colilerttest and is recommended for marine water samples.

18 Descriptions of the Colilert, Colilert-18, Quanti-Tray, and Quanti-Tray/2000 may be obtained from IDEXX Laboratories, Inc.

19 A description of the mColiBlue24test, is available from Hach Company.

20 Method 1681: Fecal Coliforms in Sewage Sludge (Biosolids) by Multiple-Tube Fermentation using A–1 Medium, EPA–821– R–06–013. July 2006. U.S. EPA.

21 Recommended for enumeration of target organism in wastewater effluent.

22 Method 1603: Escherichia coli (E. coli ) in Water by Membrane Filtration Using Modified membrane-Thermotolerant Esch- erichia coli Agar (modified mTEC), EPA–821–R–09–007. December 2009. U.S. EPA.

23 Method 1682: Salmonella in Sewage Sludge (Biosolids) by Modified Semisolid Rappaport-Vassiliadis (MSRV) Medium, EPA–821–R–06–014. July 2006. U.S. EPA.

24 A description of the Enterolerttest may be obtained from IDEXX Laboratories Inc.

25 Method 1600: Enterococci in Water by Membrane Filtration Using membrane-Enterococcus Indoxyl-b-D–Glucoside Agar (mEI), EPA–821–R–09–016. December 2009. U.S. EPA.

26 Methods for Measuring the Acute Toxicity of Effluents and Receiving Waters to Freshwater and Marine Organisms. EPA– 821–R–02–012. Fifth Edition, October 2002. U.S. EPA.

27 Short-term Methods for Estimating the Chronic Toxicity of Effluents and Receiving Waters to Freshwater Organisms. EPA– 821–R–02–013. Fourth Edition, October 2002. U.S. EPA.

28 Short-term Methods for Estimating the Chronic Toxicity of Effluents and Receiving Waters to Marine and Estuarine Orga- nisms. EPA–821–R–02–014. Third Edition, October 2002. U.S. EPA.

40 CFR Ch. I (7–1–17 Edition)

10

§ 136.3

TABLE IB—LIST OF APPROVED INORGANIC TEST PROCEDURES

| Parameter | Methodology 58 | EPA 52 | Standard methods | ASTM | USGS/AOAC/Other |
| --- | --- | --- | --- | --- | --- |
| 1. Acidity, as CaCO3, mg/L .. | Electrometric endpoint or phenolphthalein end- | .......................................... | 2310 B–1997 ................... | D1067–06 ................. | I–1020–85.2 |
|  | point. |  |  |  |  |
| 2. Alkalinity, as CaCO3, mg/L | Electrometric or Colorimetric titration to pH 4.5, | .......................................... | 2320 B–1997 ................... | D1067–06 ................. | 973.43 3, I–1030–85.2 |
|  | Manual. |  |  |  |  |
|  | Automatic ........................................................... | 310.2 (Rev. 1974)1 .......... | .......................................... | .................................. | I–2030–85.2 |
| 3. Aluminum—Total,4 mg/L .. | Digestion,4 followed by any of the following: |  |  |  |  |
|  | AA direct aspiration 36 | .......................................... | 3111 D–1999 or 3111 E– | .................................. | I–3051–85.2 |
|  |  |  | 1999. |  |  |
|  | AA furnace .................................................. | .......................................... | 3113 B–2004. |  |  |
|  | STGFAA ...................................................... | 200.9, Rev. 2.2 (1994). |  |  |  |
|  | ICP/AES 36 .................................................. | 200.5, Rev 4.2 (2003) 68; | 3120 B–1999 ................... | D1976–07 ................. | I–4471–97.50 |
|  |  | 200.7, Rev. 4.4 (1994). |  |  |  |
|  | ICP/MS ........................................................ | 200.8, Rev. 5.4 (1994) .... | 3125 B–2009 ................... | D5673–05 ................. | 993.14,3 I–4471–97.50 |
|  | Direct Current Plasma (DCP) 36 ................. | .......................................... | .......................................... | D4190–08 ................. | See footnote.34 |
|  | Colorimetric (Eriochrome cyanine R) .......... | .......................................... | 3500–Al B–2001. |  |  |
| 4. Ammonia (as N), mg/L ..... | Manual distillation 6 or gas diffusion (pH >11), | 350.1, Rev. 2.0 (1993) .... | 4500–NH3 B–1997 ........... | .................................. | 973.493. |
|  | followed by any of the following: |  |  |  |  |
|  | Nesslerization .............................................. | .......................................... | .......................................... | D1426–08 (A) ........... | 973.493, I–3520–85.2 |
|  | Titration ....................................................... | .......................................... | 4500–NH3 C–1997. |  |  |
|  | Electrode ..................................................... | .......................................... | 4500–NH3 D–1997 or E– | D1426–08 (B). |  |
|  |  |  | 1997. |  |  |
|  | Manual phenate, salicylate, or other sub- | .......................................... | 4500–NH3 F–1997 ........... | .................................. | See footnote.60 |
|  | stituted phenols in Berthelot reaction |  |  |  |  |
|  | based methods. |  |  |  |  |
|  | Automated phenate, salicylate, or other | 350.130, Rev. 2.0 (1993) | 4500–NH3 G–1997 | .................................. | I–4523–85.2 |
|  | substituted phenols in Berthelot reaction |  | 4500–NH3 H–1997. |  |  |
|  | based methods. |  |  |  |  |
|  | Automated electrode ................................... | Ion Chromatography ........ | .......................................... | D6919–09 ................. | See footnote.7 |
| 5. Antimony—Total,4 mg/L ... | Digestion,4 followed by any of the following: |  |  |  |  |
|  | AA direct aspiration 36 ................................. | .......................................... | 3111 B–1999. |  |  |
|  | AA furnace .................................................. | .......................................... | 3113 B–2004. |  |  |
|  | STGFAA ...................................................... | 200.9, Rev. 2.2 (1994). |  |  |  |
|  | ICP/AES 36 .................................................. | 200.5, Rev 4.2 (2003) 68; | 3120 B–1999 ................... | D1976–07 ................. | I–4471–97.50 |
|  |  | 200.7, Rev. 4.4 (1994). |  |  |  |
|  | ICP/MS ........................................................ | 200.8, Rev. 5.4 (1994) .... | 3125 B–2009 ................... | D5673–05 ................. | 993.14,3 I–4471–97.50 |
| 6. Arsenic–Total,4 mg/L ........ | Digestion,4 followed by any of the following: | 206.5 (Issued 1978) 1. |  |  |  |
|  | AA gaseous hydride .................................... | .......................................... | 3114 B–2009 or ............... | D2972–08 (B) ........... | I–3062–85.2 |
|  |  |  | 3114 C–2009 ................... |  |  |
|  | AA furnace .................................................. | .......................................... | 3113 B–2004 ................... | D2972–08 (C) .......... | I–4063–98.49 |
|  | STGFAA ...................................................... | 200.9, Rev. 2.2 (1994). |  |  |  |
|  | ICP/AES 36 .................................................. | 200.5, Rev 4.2 (2003) 68; | 3120 B–1999 ................... | D1976–07. |  |
|  |  | 200.7, Rev. 4.4 (1994). |  |  |  |
|  | ICP/MS ........................................................ | 200.8, Rev. 5.4 (1994) .... | 3125 B–2009 ................... | D5673–05 ................. | 993.14,3 I–4020–05.70 |
|  | Colorimetric (SDDC) ................................... | .......................................... | 3500–As B–1997 ............. | D2972–08 (A) ........... | I–3060–85.2 |
| 7. Barium–Total,4 mg/L ........ | Digestion4, followed by any of the following: |  |  |  |  |
|  | AA direct aspiration 36 ................................. | .......................................... | 3111 D–1999 ................... | .................................. | I–3084–85.2 |

Environmental Protection Agency

AA furnace ..................................................    ..........................................   3113 B–2004 ...................   D4382–02(07).

ICP/AES 36   ..................................................    200.5, Rev 4.2 (2003) 68;

200.7, Rev. 4.4 (1994).

3120 B–1999 ...................    ..................................   I–4471–97.50

ICP/MS ........................................................  200.8, Rev. 5.4 (1994) ....  3125 B–2009 ...................  D5673–05 .................  993.14,3 I–4471–97.50 DCP 36 .........................................................  ..........................................  ..........................................  ..................................  See footnote.34

- Beryllium—Total,4  mg/L  ...   Digestion,4  followed by any of the following:

AA direct aspiration .....................................    ..........................................   3111 D–1999 or ...............

3111 E–1999 ...................

D3645–08 (A) ...........   I–3095–85.2

AA furnace ..................................................    ..........................................   3113 B–2004 ...................   D3645–08 (B). STGFAA ......................................................   200.9, Rev. 2.2 (1994).

ICP/AES ......................................................    200.5, Rev 4.2 (2003) 68;

200.7, Rev. 4.4 (1994).

3120 B–1999 ...................   D1976–07 .................   I–4471–97.50

- Biochemical oxygen de- mand (BOD5), mg/L.

ICP/MS ........................................................   200.8, Rev. 5.4 (1994)  ....   3125 B–2009 ...................   D5673–05 .................   993.14,3 I–4471–97.50 DCP .............................................................    ..........................................    ..........................................   D4190–08 .................   See footnote.34 Colorimetric (aluminon) ...............................    ..........................................   See footnote 61.

Dissolved Oxygen Depletion ..............................    ..........................................   5210 B–2001 ...................    ..................................   973.443, p. 17.9, I–1578–

78,8 See footnote.10 63

10. Boron—Total,37 mg/L .....   Colorimetric (curcumin) ......................................    ..........................................   4500–B B–2000 ...............    ..................................   I–3112–85.2

ICP/AES ......................................................   200.5, Rev 4.2 (2003) 68;

200.7, Rev. 4.4 (1994).

3120 B–1999 ...................   D1976–07 .................   I–4471–97.50

ICP/MS ........................................................   200.8, Rev. 5.4 (1994)  ....   3125 B–2009 ...................   D5673–05 .................   993.14,3 I–4471–97.50 DCP .............................................................    ..........................................    ..........................................   D4190–08 .................   See footnote.34

11. Bromide, mg/L ................   Electrode ............................................................    ..........................................    ..........................................   D1246–05 .................   I–1125–85.2

Ion Chromatography ...................................   300.0, Rev 2.1 (1993)

and 300.1–1, Rev 1.0

(1997).

4110 B–2000, C–2000, D–2000.

D4327–03	993.30.3

CIE/UV ........................................................    ..........................................   4140 B–1997 ...................   D6508–00(05) ..........   D6508, Rev. 2.54

- Cadmium—Total,4  mg/L	Digestion,4 followed by any of the following:

AA direct aspiration 36  .................................    ..........................................   3111 B–1999 ...................

or 3111 C–1999 ...............

D3557–02(07) (A or B).

974.27,3 p. 37.9, I–3135–

85 2  or I–3136–85.2

AA furnace ..................................................    ..........................................   3113 B–2004 ...................   D3557–02(07) (D) ....   I–4138–89.51 STGFAA ......................................................   200.9, Rev. 2.2 (1994).

ICP/AES 36   ..................................................    200.5, Rev 4.2 (2003) 68;

200.7, Rev. 4.4 (1994).

3120 B–1999 ...................   D1976–07 .................   I–1472–85 2 or I–4471–

97.50

ICP/MS ........................................................   200.8, Rev. 5.4 (1994)  ....   3125 B–2009 ...................   D5673–05 .................   993.14,3  I–4471–97.50 DCP36   .........................................................    ..........................................    ..........................................   D4190–08 .................   See footnote.34

Voltametry11  ................................................    ..........................................    ..........................................   D3557–02(07) (C). Colorimetric (Dithizone)  ..............................    ..........................................   3500–Cd-D–1990.

- Calcium—Total,4 mg/L ...   Digestion,4 followed by any of the following:

AA direct aspiration .....................................    ..........................................   3111 B–1999 ...................   D511–08(B) ..............   I–3152–85.2

ICP/AES ......................................................    200.5, Rev 4.2 (2003) 68;

200.7, Rev. 4.4 (1994).

3120 B–1999  ...................    ..................................    I–4471–97.50

ICP/MS ........................................................   200.8, Rev. 5.4 (1994)  ....   3125 B–2009 ...................   D5673–05	993.14.3

§ 136.3

DCP .............................................................    ..........................................    ..........................................    ..................................   See footnote.34 Titrimetric (EDTA) .......................................    ..........................................   3500–Ca B–1997 .............   D511–08 (A).

Ion Chromatography ...................................    ..........................................    ..........................................   D6919–09.

- Carbonaceous bio- chemical oxygen demand (CBOD5),  mg/L12.

Dissolved Oxygen Depletion with nitrification in- hibitor.

..........................................  5210 B–2001 ...................   ..................................  See footnote.35 63

11

40 CFR Ch. I (7–1–17 Edition)

12

§ 136.3

TABLE IB—LIST OF APPROVED INORGANIC TEST PROCEDURES—Continued

| Parameter | Methodology 58 | EPA 52 | Standard methods | ASTM | USGS/AOAC/Other |
| --- | --- | --- | --- | --- | --- |
| 15. Chemical oxygen de- | Titrimetric ............................................................ | 410.3 (Rev. 1978)1 .......... | 5220 B–1997 ................... | D1252–06 (A) ........... | 973.46,3 p. 17,9 I–3560– |
| mand (COD), mg/L. |  |  | or C–1997 ........................ |  | 85.2 |
|  | Spectrophotometric, manual or automatic ......... | 410.4, Rev. 2.0 (1993) .... | 5220 D–1997 ................... | D1252–06 (B) ........... | See footnotes.13 14 I– |
|  |  |  |  |  | 3561–85.2 |
| 16. Chloride, mg/L ................ | Titrimetric: (silver nitrate) ................................... | .......................................... | 4500–Cl¥ B–1997 ........... | D512–04 (B) ............. | I–1183–85.2 |
|  | (Mercuric nitrate) ................................................ | .......................................... | 4500–Cl¥ C–1997 ........... | D512–04 (A) ............. | 973.51,3 I–1184–85.2 |
|  | Colorimetric: manual .......................................... | .......................................... | .......................................... | .................................. | I–1187–85.2 |
|  | Automated (Ferricyanide) ................................... | .......................................... | 4500–Cl¥ E–1997 ........... | .................................. | I–2187–85.2 |
|  | Potentiometric Titration ...................................... | .......................................... | 4500–Cl¥ D–1997. |  |  |
|  | Ion Selective Electrode ...................................... | .......................................... | .......................................... | D512–04 (C). |  |
|  | Ion Chromatography .......................................... | 300.0, Rev 2.1 (1993) | 4110 B–2000 or ............... | D4327–03 ................. | 993.303 , I–2057–90.51 |
|  |  | and 300.1–1, Rev 1.0 | 4110 C–2000 ................... |  |  |
|  |  | (1997). |  |  |  |
|  | CIE/UV ............................................................... | .......................................... | 4140 B–1997 ................... | D6508–00(05) .......... | D6508, Rev. 2.54 |
| 17. Chlorine–Total residual, | Amperometric direct ........................................... | .......................................... | 4500–Cl D–2000 .............. | D1253–08. |  |
| mg/L. |  |  |  |  |  |
|  | Amperometric direct (low level) ......................... | .......................................... | 4500–Cl E–2000. |  |  |
|  | Iodometric direct ................................................. | .......................................... | 4500–Cl B–2000. |  |  |
|  | Back titration ether end-point15 .......................... | .......................................... | 4500–Cl C–2000. |  |  |
|  | DPD–FAS ........................................................... | .......................................... | 4500–Cl F–2000. |  |  |
|  | Spectrophotometric, DPD .................................. | .......................................... | 4500–Cl G–2000. |  |  |
|  | Electrode ............................................................ | .......................................... | .......................................... | .................................. | See footnote.16 |
| 17A. Chlorine–Free Avail- | Amperometric direct ........................................... | .......................................... | 4500–Cl D–2000 .............. | D1253–08. |  |
| able, mg/L. |  |  |  |  |  |
|  | Amperometric direct (low level) ......................... | .......................................... | 4500–Cl E–2000. |  |  |
|  | DPD–FAS ........................................................... | .......................................... | 4500–Cl F–2000. |  |  |
|  | Spectrophotometric, DPD .................................. | .......................................... | 4500–Cl G–2000. |  |  |
| 18. Chromium VI dissolved, | 0.45-micron Filtration followed by any of the fol- |  |  |  |  |
| mg/L. | lowing: |  |  |  |  |
|  | AA chelation-extraction ............................... | .......................................... | 3111 C–1999 ................... | .................................. | I–1232–85.2 |
|  | Ion Chromatography ................................... | 218.6, Rev. 3.3 (1994) .... | 3500–Cr C–2009 ............. | D5257–03 ................. | 993.23. |
|  | Colorimetric (Diphenyl-carbazide) ............... | .......................................... | 3500–Cr B–2009 ............. | D1687–02(07) (A) .... | I–1230–85.2 |
| 19. Chromium—Total,4 mg/L | Digestion,4 followed by any of the following: |  |  |  |  |
|  | AA direct aspiration 36 ................................. | .......................................... | 3111 B–1999 ................... | D1687–02(07) (B) .... | 974.27,3 I–3236–85.2 |
|  | AA chelation-extraction ............................... | .......................................... | 3111 C–1999. |  |  |
|  | AA furnace .................................................. | .......................................... | 3113 B–2004 ................... | D1687–02(07) (C) .... | I–3233–93.46 |
|  | STGFAA ...................................................... | 200.9, Rev. 2.2 (1994). |  |  |  |
|  | ICP/AES 36 .................................................. | 200.5, Rev 4.2 (2003),68 | 3120 B–1999 ................... | D1976–07 ................. | I–4471–97.50 |
|  |  | 200.7, Rev. 4.4 (1994). |  |  |  |
|  | ICP/MS ........................................................ | 200.8, Rev. 5.4 (1994) .... | 3125 B–2009 ................... | D5673–05 ................. | 993.14,3 I–4020–05.70 |
|  | DCP 36 ......................................................... | .......................................... | .......................................... | D4190–08 ................. | See footnote.34 |
|  | Colorimetric (Diphenyl-carbazide) ............... | .......................................... | 3500–Cr B–2009. |  |  |
| 20. Cobalt—Total,4 mg/L ...... | Digestion,4 followed by any of the following: |  |  |  |  |
|  | AA direct aspiration ..................................... | .......................................... | 3111 B–1999 or 3111 C– | D3558–08 (A or B) ... | p. 37,9 I–3239–85.2 |
|  |  |  | 1999. |  |  |
|  | AA furnace .................................................. | .......................................... | 3113 B–2004 ................... | D3558–08 (C) .......... | I–4243–89.51 |

STGFAA ......................................................   200.9, Rev. 2.2 (1994).

ICP/AES 36  ..................................................  200.5, Rev 4.2 (2003) 68;

200.7, Rev. 4.4 (1994).

Environmental Protection Agency

3120 B–1999  ...................    D1976–07 .................    I–4471–97.50

- Color, platinum cobalt units or dominant wave- length, hue, luminance pu- rity.

ICP/MS ........................................................   200.8, Rev. 5.4 (1994)  ....   3125 B–2009 ...................   D5673–05 .................   993.14,3  I–4020–05.70 DCP .............................................................    ..........................................    ..........................................   D4190–08 .................   See footnote.34

Colorimetric (ADMI)	..........................................    ..........................................    ..................................   See footnote.18

(Platinum cobalt) ................................................    ..........................................   2120 B–2001 ...................    ..................................   I–1250–85.2

Spectrophotometric.

- Copper—Total,4 mg/L  ....   Digestion,4 followed by any of the following:

AA direct aspiration 36 .................................  ..........................................  3111 B–1999 or ...............

3111 C–1999 ...................

D1688–07 (A or B) ...    974.27,3  p. 37,9  I–3270–

85 2 or I–3271–85.2

AA furnace ..................................................    ..........................................   3113 B–2004 ...................   D1688–07 (C)  ..........   I–4274–89.51 STGFAA ......................................................   200.9, Rev. 2.2 (1994).

ICP/AES 36  ..................................................  200.5, Rev 4.2 (2003) 68;

200.7, Rev. 4.4 (1994).

3120 B–1999  ...................    D1976–07 .................    I–4471–97.50

ICP/MS ........................................................   200.8, Rev. 5.4 (1994)  ....   3125 B–2009 ...................   D5673–05 .................   993.14,3 I–4020–05.70 DCP 36  .........................................................    ..........................................    ..........................................   D4190–08 .................   See footnote.34 Colorimetric (Neocuproine) .........................    ..........................................   3500–Cu B–1999.

(Bathocuproine) ...........................................    ..........................................   3500–Cu C–1999  ............    ..................................   See footnote.19

- Cyanide—Total, mg/L  ....   Automated  UV  digestion/distillation  and  Col- orimetry.

Segmented Flow Injection, In-Line Ultraviolet Digestion, followed by gas diffusion amper- ometry.

..........................................    ..........................................    ..................................   Kelada–01.55

..........................................    ..........................................   D7511–09.

Manual distillation with MgCl2, followed by any of the following:

335.4, Rev. 1.0 (1993) 57	4500–CN¥ B–1999 or C–

1999.

D2036–09(A), D7284–08.

10–204–00–1–X.56

Flow Injection, gas diffusion amperometry	..........................................    ..........................................   D2036–09(A)

D7284–08.

Titrimetric  ....................................................    ..........................................    4500–CN¥ D–1999 .........    D2036–09(A) ............    p. 22.9

Spectrophotometric, manual .......................    ..........................................    4500–CN¥ E–1999  .........    D2036–09(A) ............    I–3300–85.2

Semi-Automated 20 ......................................  335.4, Rev. 1.0 (1993) 57	..........................................  .................................. 10–204–00–1–X,56 I–

4302–85.2

Ion Chromatography ...................................    ..........................................    ..........................................   D2036–09(A).

Ion Selective Electrode ...............................    ..........................................    4500–CN¥ F–1999  .........    D2036–09(A).

- Cyanide–Available, mg/L    Cyanide   Amenable   to   Chlorination   (CATC);

Manual  distillation  with  MgCl2,  followed  by Titrimetric or Spectrophotometric.

Flow  injection  and  ligand  exchange,  followed by gas diffusion amperometry 59.

Automated Distillation and Colorimetry (no UV digestion).

24.A Cyanide-Free, mg/L .....   Flow Injection, followed by gas diffusion amper-

ometry.

..........................................    4500–CN¥  G–1999 .........    D2036–09(B).

..........................................    ..........................................   D6888–09 .................   OIA–1677–09.44

..........................................    ..........................................    ..................................   Kelada–01.55

..........................................    ..........................................   D7237–10 .................    OIA–1677–09.44

§ 136.3

Manual micro-diffusion and colorimetry .............    ..........................................    ..........................................   D4282–02.

- Fluoride—Total, mg/L .....   Manual distillation,6  followed by any of the fol-

lowing:

..........................................    4500–F¥  B–1997.

13

Electrode, manual .......................................    ..........................................    4500–F¥ C–1997 ............    D1179–04 (B).

40 CFR Ch. I (7–1–17 Edition)

14

§ 136.3

TABLE IB—LIST OF APPROVED INORGANIC TEST PROCEDURES—Continued

| Parameter | Methodology 58 | EPA 52 | Standard methods | ASTM | USGS/AOAC/Other |
| --- | --- | --- | --- | --- | --- |
| 26. Gold—Total,4 mg/L ........ | Electrode, automated .................................. | .......................................... | .......................................... | .................................. | I–4327–85.2 |
|  | Colorimetric, (SPADNS) .............................. | .......................................... | 4500–F¥ D–1997 ............ | D1179–04 (A). |  |
|  | Automated complexone .............................. | .......................................... | 4500–F¥ E–1997. |  |  |
|  | Ion Chromatography ................................... | 300.0, Rev 2.1 (1993) | 4110 B–2000 or C–2000 | D4327–03 ................. | 993.30.3 |
|  |  | and 300.1–1, Rev 1.0 |  |  |  |
|  |  | (1997). |  |  |  |
|  | CIE/UV ........................................................ | .......................................... | 4140 B–1997 ................... | D6508–00(05) .......... | D6508, Rev. 2.54 |
|  | Digestion,4 followed by any of the following: |  |  |  |  |
|  | AA direct aspiration ..................................... | .......................................... | 3111 B–1999. |  |  |
|  | AA furnace .................................................. | 231.2 (Issued 1978)1 ....... | 3113 B–2004. |  |  |
|  | ICP/MS ........................................................ | 200.8, Rev. 5.4 (1994) .... | 3125 B–2009 ................... | D5673–05 ................. | 993.14.3 |
|  | DCP ............................................................. | .......................................... | .......................................... | .................................. | See footnote.34 |
| 27. Hardness—Total, as | Automated colorimetric ...................................... | 130.1 (Issued 1971)1. |  |  |  |
| CaCO3, mg/L. |  |  |  |  |  |
|  | Titrimetric (EDTA) .............................................. | .......................................... | 2340 C–1997 ................... | D1126–02(07) .......... | 973.52B,3 I–1338–85.2 |
|  | Ca plus Mg as their carbonates, by inductively | .......................................... | 2340 B–1997. |  |  |
|  | coupled plasma or AA direct aspiration. (See |  |  |  |  |
|  | Parameters 13 and 33).. |  |  |  |  |
| 28. Hydrogen ion (pH), pH | Electrometric measurement ............................... | .......................................... | 4500–H + B–2000 ...... | D1293–99 (A or B) ... | 973.41,3 I–1586–85.2 |
| units. |  |  |  |  |  |
|  | Automated electrode .......................................... | 150.2 (Dec. 1982)1 .......... | .......................................... | .................................. | See footnote,21 I–2587– |
|  |  |  |  |  | 85.2 |
| 29. Iridium—Total,4 mg/L ..... | Digestion,4 followed by any of the following: |  |  |  |  |
|  | AA direct aspiration ..................................... | .......................................... | 3111 B–1999. |  |  |
|  | AA furnace .................................................. | 235.2 (Issued 1978)1. |  |  |  |
|  | ICP/MS ........................................................ | .......................................... | 3125 B–2009. |  |  |
| 30. Iron—Total,4 mg/L .......... | Digestion,4 followed by any of the following: |  |  |  |  |
|  | AA direct aspiration 36 ................................. | .......................................... | 3111 B–1999 or ............... | D1068–05 (A or B) ... | 974.27,3 I–3381–85.2 |
|  |  |  | 3111 C–1999 ................... |  |  |
|  | AA furnace .................................................. | .......................................... | 3113 B–2004 ................... | D1068–05 (C). |  |
|  | STGFAA ...................................................... | 200.9, Rev. 2.2 (1994). |  |  |  |
|  | ICP/AES 36 .................................................. | 200.5, Rev 4.2 (2003) 68; | 3120 B–1999 ................... | D1976–07 ................. | I–4471–97.50 |
|  |  | 200.7, Rev. 4.4 (1994). |  |  |  |
|  | ICP/MS ........................................................ | 200.8, Rev. 5.4 (1994) .... | 3125 B–2009 ................... | D5673–05 ................. | 993.14.3 |
|  | DCP 36 ......................................................... | .......................................... | .......................................... | D4190–08 ................. | See footnote.34 |
|  | Colorimetric (Phenanthroline) ..................... | .......................................... | 3500–Fe-1997 ................. | D1068–05 (D) .......... | See footnote.22 |
| 31. Kjeldahl Nitrogen 5— | Manual digestion 20 and distillation or gas diffu- | .......................................... | 4500–Norg B–1997 or C– | D3590–02(06) (A) .... | I–4515–91.45 |
| Total, (as N), mg/L. | sion, followed by any of the following: |  | 1997 and 4500–NH3 B– |  |  |
|  |  |  | 1997. |  |  |
|  | Titration ....................................................... | .......................................... | 4500–NH3 C–1997 .......... | .................................. | 973.48.3 |
|  | Nesslerization .............................................. | .......................................... | .......................................... | D1426–08 (A). |  |
|  | Electrode ..................................................... | .......................................... | 4500–NH3 D–1997 or E– | D1426–08 (B). |  |
|  |  |  | 1997. |  |  |
|  | Semi-automated phenate ............................ | 350.1 Rev 2.0 1993 ......... | 4500–NH3 G–1997. |  |  |
|  |  |  | 4500–NH3 H–1997. |  |  |

15

- Environmental Protection Agency

| Manual phenate, salicylate, or other sub- stituted phenols in Berthelot reaction based methods. | .......................................... | 4500–NH3 F–1997 ........... | .................................. | See footnote.60 |
| --- | --- | --- | --- | --- |
| Automated Methods for TKN that do not require manual distillation |
| Automated phenate, salicylate, or other sub- | 351.1 (Rev. 1978)1 .......... | .......................................... | .................................. | I–4551–78.8 |
| stituted phenols in Berthelot reaction based |  |  |  |  |
| methods colorimetric (auto digestion and dis- |  |  |  |  |
| tillation). |  |  |  |  |
| Semi-automated block digestor colorimetric | 351.2, Rev. 2.0 (1993) .... | 4500–Norg D–1997 ........... | D3590–02(06) (B) .... | I–4515–91.45 |
| (distillation not required). |  |  |  |  |
| Block digester, followed by Auto distillation and | .......................................... | .......................................... | .................................. | See footnote.39 |
| Titration. |  |  |  |  |
| Block digester, followed by Auto distillation and | .......................................... | .......................................... | .................................. | See footnote.40 |
| Nesslerization. |  |  |  |  |
| Block Digester, followed by Flow injection gas | .......................................... | .......................................... | .................................. | See footnote.41 |
| diffusion (distillation not required). |  |  |  |  |
| Digestion,4 followed by any of the following: |  |  |  |  |
| AA direct aspiration 36 ................................. | .......................................... | 3111 B–1999 or ............... | D3559–08 (A or B) ... | 974.27,3 I–3399–85.2 |
|  |  | 3111 C–1999. |  |  |
| AA furnace .................................................. | .......................................... | 3113 B–2004 ................... | D3559–08 (D) .......... | I–4403–89.51 |
| STGFAA ...................................................... | 200.9, Rev. 2.2 (1994). |  |  |  |
| ICP/AES 36 .................................................. | 200.5, Rev 4.2 (2003)68; | 3120 B–1999 ................... | D1976–07 ................. | I–4471–97.50 |
|  | 200.7, Rev. 4.4 (1994). |  |  |  |
| ICP/MS ........................................................ | 200.8, Rev. 5.4 (1994) .... | 3125 B–2009 ................... | D5673–05 ................. | 993.14,3 I–4471–97.50 |
| DCP 36 ......................................................... | .......................................... | .......................................... | D4190–08 ................. | See footnote.34 |
| Voltametry11 ................................................ | .......................................... | .......................................... | D3559–08 (C). |  |
| Colorimetric (Dithizone) .............................. | .......................................... | 3500–Pb B–1997. |  |  |
| Digestion,4 followed by any of the following: |  |  |  |  |
| AA direct aspiration ..................................... | .......................................... | 3111 B–1999 ................... | D511–08 (B) ............. | 974.27,3 I–3447–85.2 |
| ICP/AES ...................................................... | 200.5, Rev 4.2 (2003) 68; | 3120 B–1999 ................... | D1976–07 ................. | I–4471–97.50 |
|  | 200.7, Rev. 4.4 (1994). |  |  |  |
| ICP/MS ........................................................ | 200.8, Rev. 5.4 (1994) .... | 3125 B–2009 ................... | D5673–05 ................. | 993.14.3 |
| DCP ............................................................. | .......................................... | .......................................... | .................................. | See footnote.34 |
| Gravimetric. |  |  |  |  |
| Ion Chromatography ................................... | .......................................... | .......................................... | D6919–09. |  |
| Digestion 4 followed by any of the following: |  |  |  |  |
| AA direct aspiration 36 ................................. | .......................................... | 3111 B–1999 ................... | D858–07 (A or B) ..... | 974.27,3 I–3454–85.2 |
| AA furnace .................................................. | .......................................... | 3113 B–2004 ................... | D858–07 (C). |  |
| STGFAA ...................................................... | 200.9, Rev. 2.2 (1994). |  |  |  |
| ICP/AES 36 .................................................. | 200.5, Rev 4.2 (2003) 68; | 3120 B–1999 ................... | D1976–07 ................. | I–4471–97.50 |
|  | 200.7, Rev. 4.4 (1994). |  |  |  |
| ICP/MS ........................................................ | 200.8, Rev. 5.4 (1994) .... | 3125 B–2009 ................... | D5673–05 ................. | 993.14,3 I–4471–97.50 |
| DCP 36 ......................................................... | .......................................... | .......................................... | D4190–08 ................. | See footnote.34 |
| Colorimetric (Persulfate) ............................. | .......................................... | 3500–Mn B–1999 ............ | .................................. | 920.203.3 |
| (Periodate) .................................................. | .......................................... | .......................................... | .................................. | See footnote.23 |
| Cold vapor, Manual ............................................ | 245.1, Rev. 3.0 (1994) .... | 3112 B–2009 ................... | D3223–02(07) .......... | 977.22,3 I–3462–85.2 |

Lead—Total,4 mg/L ........

- Magnesium—Total,4  mg/ L.

- Manganese—Total,4  mg/ L.

- § 136.3

Mercury—Total,4  mg/L ...

40 CFR Ch. I (7–1–17 Edition)

16

§ 136.3

TABLE IB—LIST OF APPROVED INORGANIC TEST PROCEDURES—Continued

| Parameter | Methodology 58 | EPA 52 | Standard methods | ASTM | USGS/AOAC/Other |
| --- | --- | --- | --- | --- | --- |
| 36. Molybdenum—Total,4 | Cold vapor, Automated ...................................... | 245.2 (Issued 1974)1. | .......................................... | .................................. | I–4464–01.71 |
|  | Cold vapor atomic fluorescence spectrometry | 245.7 Rev. 2.0 (2005)17 .. |  |  |  |
|  | (CVAFS). |  |  |  |  |
|  | Purge and Trap CVAFS ..................................... | 1631E43. |  |  |  |
|  | Digestion,4 followed by any of the following: |  |  |  |  |
| mg/L. |  |  |  |  |  |
|  | AA direct aspiration ..................................... | .......................................... | 3111 D–1999 ................... | .................................. | I–3490–85.2 |
|  | AA furnace .................................................. | .......................................... | 3113 B–2004 ................... | .................................. | I–3492–96.47 |
|  | ICP/AES 36 .................................................. | 200.5, Rev 4.2 (2003) 68; | 3120 B–1999 ................... | D1976–07 ................. | I–4471–97.50 |
|  |  | 200.7, Rev. 4.4 (1994). |  |  |  |
|  | ICP/MS ........................................................ | 200.8, Rev. 5.4 (1994) .... | 3125 B–2009 ................... | D5673–05 ................. | 993.14,3 I–4471–97.50 |
|  | DCP ............................................................. | .......................................... | .......................................... | .................................. | See footnote.34 |
| 37. Nickel—Total,4 mg/L ...... | Digestion 4 followed by any of the following: |  |  |  |  |
|  | AA direct aspiration 36 ................................. | .......................................... | 3111 B–1999 or ............... | D1886–08 (A or B) ... | I–3499–85.2 |
|  |  |  | 3111 C–1999 ................... |  |  |
|  | AA furnace .................................................. | .......................................... | 3113 B–2004 ................... | D1886–08 (C) .......... | I–4503–89.51 |
|  | STGFAA ...................................................... | 200.9, Rev. 2.2 (1994). |  |  |  |
|  | ICP/AES 36 .................................................. | 200.5, Rev 4.2 (2003) 68; | 3120 B–1999 ................... | D1976–07 ................. | I–4471–97.50 |
|  |  | 200.7, Rev. 4.4 (1994). |  |  |  |
|  | ICP/MS ........................................................ | 200.8, Rev. 5.4 (1994) .... | 3125 B–2009 ................... | D5673–05 ................. | 993.14,3 I–4020–05.70 |
|  | DCP 36 ......................................................... | .......................................... | .......................................... | D4190–08 ................. | See footnote.34 |
| 38. Nitrate (as N), mg/L ....... | Ion Chromatography .......................................... | 300.0, Rev 2.1 (1993) | 4110 B–2000 or C–2000 | D4327–03 ................. | 993.30.3 |
|  |  | and 300.1–1, Rev 1.0 |  |  |  |
|  |  | (1997). |  |  |  |
|  | CIE/UV ........................................................ | .......................................... | 4140 B–1997 ................... | D6508–00(05) .......... | D6508, Rev. 2.54 |
|  | Ion Selective Electrode ............................... | .......................................... | 4500–NO ¥ D–2000. 3 |  |  |
|  | Colorimetric (Brucine sulfate) ..................... | 352.1 (Issued 1971)1 ....... | .......................................... | .................................. | 973.50,3 419D1 7, p. 28.9 |
|  | Nitrate-nitrite N minus Nitrite N (See pa- | .......................................... | .......................................... | .................................. | See footnote.62 |
|  | rameters 39 and 40). |  |  |  |  |
| 39. Nitrate-nitrite (as N), mg/ | Cadmium reduction, Manual .............................. | .......................................... | 4500–NO ¥ E–2000 ........ 3 | D3867–04 (B). |  |
| L. |  |  |  |  |  |
|  | Cadmium reduction, Automated ................. | 353.2, Rev. 2.0 (1993) .... | 4500–NO ¥ F–2000 ........ 3 | D3867–04 (A) ........... | I–2545–90.51 |
|  | Automated hydrazine .................................. | .......................................... | 4500–NO ¥ H–2000. 3 |  |  |
|  | Reduction/Colorimetric ................................ | .......................................... | .......................................... | .................................. | See footnote.62 |
|  | Ion Chromatography ................................... | 300.0, Rev 2.1 (1993) | 4110 B–2000 or C–2000 | D4327–03 ................. | 993.30.3 |
|  |  | and 300.1–1, Rev 1.0 |  |  |  |
|  |  | (1997). |  |  |  |
|  | CIE/UV ........................................................ | .......................................... | 4140 B–1997 ................... | D6508–00(05) .......... | D6508, Rev. 2.54 |
| 40. Nitrite (as N), mg/L ......... | Spectrophotometric: Manual .............................. | .......................................... | 4500–NO ¥ B–2000 ........ 2 | .................................. | See footnote.25 |
|  | Automated (Diazotization) ........................... | .......................................... | .......................................... | .................................. | I–4540–852, See foot- |
|  |  |  |  |  | note.62 |
|  | Automated (*bypass cadmium reduction) ... | 353.2, Rev. 2.0 (1993) .... | 4500–NO ¥ F–2000 ........ 3 | D3867–04 (A) ........... | I–4545–85.2 |
|  | Manual (*bypass cadmium reduction) ........ | .......................................... | 4500–NO ¥ E–2000 ........ 3 | D3867–04 (B). |  |
|  | Ion Chromatography ................................... | 300.0, Rev 2.1 (1993) | 4110 B–2000 or C–2000 | D4327–03 ................. | 993.30.3 |
|  |  | and 300.1–1, Rev 1.0 |  |  |  |
|  |  | (1997). |  |  |  |

Environmental Protection Agency

CIE/UV ........................................................    ..........................................   4140 B–1997 ...................   D6508–00(05) ..........   D6508, Rev. 2.54

- Oil and grease—Total re- coverable, mg/L.

Hexane extractable material (HEM): n–Hexane extraction and gravimetry.

Silica gel treated HEM (SGT–HEM): Silica gel treatment and gravimetry.

1664 Rev. A; 1664 Rev. B42.

1664 Rev. A; 1664 Rev. B42.

5520 B–200138.

5520 B–200138  and 5520 F–200138.

- Organic carbon—Total (TOC), mg/L.

Combustion ........................................................    ..........................................   5310 B–2000 ...................   D7573–09 .................   973.473, p. 14.24

- Organic nitrogen (as N), mg/L.

- Ortho-phosphate (as P), mg/L.

Heated persulfate or UV persulfate oxida- tion.

Total Kjeldahl N (Parameter 31) minus ammo- nia N (Parameter 4).

..........................................   5310 C 2000 ....................

5310 D 2000.

Ascorbic acid method:

D4839–03 .................    973.473, p. 14.24

Automated ...................................................   365.1, Rev. 2.0 (1993)  ....   4500–P F–1999 or G–

1999.

..................................    973.563, I–4601–85.2

Manual single reagent  ................................    ..........................................   4500–P E–1999 ...............   D515–88(A)	973.55.3

Manual two reagent ....................................   365.3 (Issued 1978)1.

Ion Chromatography ...................................   300.0, Rev 2.1 (1993)

and 300.1–1, Rev 1.0

(1997).

4110 B–2000 or C–2000	D4327–03	993.30.3

CIE/UV ........................................................    ..........................................   4140 B–1997 ...................   D6508–00(05) ..........   D6508, Rev. 2.54

- Osmium—Total4, mg/L ...   Digestion4, followed by any of the following:

AA direct aspiration, ....................................    ..........................................   3111 D–1999. AA furnace ..................................................   252.2 (Issued 1978)1.

46. Oxygen, dissolved, mg/L     Winkler (Azide modification)  ..............................    ..........................................   4500–O B–2001, C–2001,

D–2001, E–2001, F– 2001.

D888–09 (A) .............    973.45B3, I–1575–78.8

Electrode .....................................................    ..........................................   4500–O G–2001 ..............   D888–09 (B) .............   I–1576–78.8

Luminescence Based Sensor .....................    ..........................................    ..........................................   D888–09 (C)  ............   See footnote63

See footnote.64

- Palladium—Total,4 mg/L     Digestion4, followed by any of the following:

AA direct aspiration .....................................    ..........................................   3111 B–1999. AA furnace ..................................................   253.21(Issued 1978).

ICP/MS ........................................................    ..........................................   3125 B–2009.

DCP .............................................................    ..........................................    ..........................................    ..................................   See footnote.34

- Phenols, mg/L ................   Manual distillation26, followed by any of the fol-

lowing:

420.11(Rev. 1978) ...........   5530 B–2005 ...................   D1783–01.

- Phosphorus (elemental), mg/L.

Colorimetric (4AAP) manual .......................   420.11(Rev. 1978)  ...........   5530 D–200527  ................   D1783–01 (A or B).

Automated colorimetric (4AAP)  ..................   420.4 Rev. 1.0 (1993).

Gas-liquid chromatography ................................    ..........................................    ..........................................    ..................................   See footnote.28

50. Phosphorus—Total, mg/L    Digestion20, followed by any of the following:	..........................................   4500–P B(5)-1999	973.55.3

Manual  ........................................................   365.31(Issued 1978) ........   4500–P E–1999 ...............   D515–88 (A).

Automated ascorbic acid reduction  ............   365.1 Rev. 2.0 (1993)  .....   4500–P F–1999, G–1999,

H–1999.

..................................    973.563, I–4600–85.2

§ 136.3

ICP/AES4 36   ................................................   200.7, Rev. 4.4 (1994)  ....   3120 B–1999 ...................    ..................................   I–4471–97.50

Semi-automated  block  digestor  (TKP  di- gestion).

51. Platinum—Total,4  mg/L ..   Digestion4  followed by any of the following:

365.41 (Issued 1974) .......    ..........................................   D515–88 (B) .............   I–4610–91.48

17

AA direct aspiration .....................................    ..........................................   3111 B–1999.

40 CFR Ch. I (7–1–17 Edition)

18

§ 136.3

TABLE IB—LIST OF APPROVED INORGANIC TEST PROCEDURES—Continued

| Parameter | Methodology 58 | EPA 52 | Standard methods | ASTM | USGS/AOAC/Other |
| --- | --- | --- | --- | --- | --- |
| 52. Potassium—Total,4 mg/L | AA furnace .................................................. | 255.2 (Issued 1978)1. | 3125 B–2009. | .................................. | See footnote.34 |
|  | ICP/MS ........................................................ | .......................................... |  |  |  |
|  | DCP ............................................................. | .......................................... | .......................................... |  |  |
|  | Digestion4, followed by any of the following: |  |  |  |  |
|  | AA direct aspiration ..................................... | .......................................... | 3111 B–1999 ................... | .................................. | 973.533, I–3630–85.2 |
|  | ICP/AES ...................................................... | 200.7, Rev. 4.4 (1994) .... | 3120 B–1999. |  |  |
|  | ICP/MS ........................................................ | 200.8, Rev. 5.4 (1994) .... | 3125 B–2009 ................... | D5673–05 ................. | 993.14.3 |
|  | Flame photometric ...................................... | .......................................... | 3500–K B–1997. |  |  |
|  | Electrode ..................................................... | .......................................... | 3500–K C–1997. |  |  |
|  | Ion Chromatography ................................... | .......................................... | .......................................... | D6919–09. |  |
| 53. Residue—Total, mg/L .... | Gravimetric, 103–105....................................... | .......................................... | 2540 B–1997 ................... | .................................. | I–3750–85.2 |
| 54. Residue—filterable, mg/L | Gravimetric, 180............................................... | .......................................... | 2540 C–1997 ................... | D5907–03 ................. | I–1750–85.2 |
| 55. Residue—non-filterable | Gravimetric, 103–105post washing of residue | .......................................... | 2540 D–1997 ................... | D5907–03 ................. | I–3765–85.2 |
| (TSS), mg/L. |  |  |  |  |  |
| 56. Residue—settleable, mg/ | Volumetric, (Imhoff cone), or gravimetric ........... | .......................................... | 2540 F–1997. |  |  |
| L. |  |  |  |  |  |
| 57. Residue—Volatile, mg/L | Gravimetric, 550............................................... | 160.4 (Issued 1971)1 ....... | 2540–E–1997 .................. | .................................. | I–3753–85.2 |
| 58. Rhodium—Total,4 mg/L .. | Digestion4 followed by any of the following: |  |  |  |  |
|  | AA direct aspiration, or ............................... | .......................................... | 3111 B–1999. |  |  |
|  | AA furnace .................................................. | 265.2 (Issued 1978)1. |  |  |  |
|  | ICP/MS ........................................................ | .......................................... | 3125 B–2009. |  |  |
| 59. Ruthenium—Total,4 mg/L | Digestion4 followed by any of the following: |  |  |  |  |
|  | AA direct aspiration, or ............................... | .......................................... | 3111 B–1999. |  |  |
|  | AA furnace .................................................. | 267.21. |  |  |  |
|  | ICP/MS ........................................................ | .......................................... | 3125 B–2009. |  |  |
| 60. Selenium—Total,4 mg/L | Digestion4, followed by any of the following: |  |  |  |  |
|  | AA furnace .................................................. | .......................................... | 3113 B–2004 ................... | D3859–08 (B) ........... | I–4668–98.49 |
|  | STGFAA ...................................................... | 200.9, Rev. 2.2 (1994). |  |  |  |
|  | ICP/AES36 ................................................... | 200.5, Rev 4.2 (2003)68; | 3120 B–1999 ................... | D1976–07. |  |
|  |  | 200.7, Rev. 4.4 (1994). |  |  |  |
|  | ICP/MS ........................................................ | 200.8, Rev. 5.4 (1994) .... | 3125 B–2009 ................... | D5673–05 ................. | 993.143, I–4020–05.70 |
|  | AA gaseous hydride .................................... | .......................................... | 3114 B–2009, or 3111 C– | D3859–08 (A) ........... | I–3667–85.2 |
|  |  |  | 2009. |  |  |
| 61. Silica—Dissolved,37 mg/L | 0.45-micron filtration followed by any of the fol- |  |  |  |  |
|  | lowing: |  |  |  |  |
|  | Colorimetric, Manual ................................... | .......................................... | 4500–SiO2 C–1997 .......... | D859–05 ................... | I–1700–85.2 |
|  | Automated (Molybdosilicate) ....................... | .......................................... | 4500–SiO2 E–1997 or F– | .................................. | I–2700–85.2 |
|  |  |  | 1997. |  |  |
|  | ICP/AES ...................................................... | 200.5, Rev 4.2 (2003)68; | 3120 B–1999 ................... | .................................. | I–4471–97.50 |
|  |  | 200.7, Rev. 4.4 (1994). |  |  |  |
|  | ICP/MS ........................................................ | 200.8, Rev. 5.4 (1994) .... | 3125 B–2009 ................... | D5673–05 ................. | 993.14.3 |
| 62. Silver—Total,4 31 mg/L ... | Digestion4, 29, followed by any of the following: |  |  |  |  |
|  | AA direct aspiration ..................................... | .......................................... | 3111 B–1999 or | .................................. | 974.273, p. 379, I–3720– |
|  |  |  | 3111 C–1999 ................... |  | 85.2 |
|  | AA furnace .................................................. | .......................................... | 3113 B–2004 ................... | .................................. | I–4724–89.51 |
|  | STGFAA ...................................................... | 200.9, Rev. 2.2 (1994). |  |  |  |

ICP/AES ......................................................    200.5, Rev 4.2 (2003)68;

200.7, Rev. 4.4 (1994).

3120 B–1999  ...................    D1976–07 .................    I–4471–97.50

ICP/MS ........................................................   200.8, Rev. 5.4 (1994)  ....   3125 B–2009 ...................   D5673–05 .................   993.143, I–4471–97.50 DCP .............................................................    ..........................................    ..........................................    ..................................   See footnote.34

- Sodium—Total,4 mg/L ....   Digestion4, followed by any of the following:

AA direct aspiration .....................................    ..........................................   3111 B–1999 ...................    ..................................   973.543, I–3735–85.2

ICP/AES ......................................................    200.5, Rev 4.2 (2003)68;

200.7, Rev. 4.4 (1994).

3120 B–1999  ...................    ..................................    I–4471–97.50

- Specific conductance, micromhos/cm at 25 C.

ICP/MS ........................................................   200.8, Rev. 5.4 (1994)  ....   3125 B–2009 ...................   D5673–05	993.14.3

DCP .............................................................    ..........................................    ..........................................    ..................................   See footnote.34 Flame photometric ......................................    ..........................................   3500–Na B–1997.

Ion Chromatography ...................................    ..........................................    ..........................................   D6919–09.

Wheatstone bridge .............................................   120.11(Rev. 1982)  ...........   2510 B–1997 ...................   D1125–95(99) (A) ....   973.403, I–2781–85.2

2¥ F–1997 or

65. Sulfate (as SO4), mg/L ...   Automated colorimetric  ......................................   375.2, Rev. 2.0 (1993)  ....   4500–SO4

G–1997.

4

Gravimetric ..................................................  .......................................... 4500–SO 2¥ C–1997 or

D–1997.

..................................    925.54.3

4

Turbidimetric ...............................................  ..........................................  4500–SO 2¥ E–1997 ......  D516–07.

Ion Chromatography ...................................   300.0, Rev 2.1 (1993)

and 300.1–1, Rev 1.0

(1997).

4110 B–2000 or C–2000	D4327–03 .................    993.303, I–4020–05.70

Environmental Protection Agency

CIE/UV ........................................................    ..........................................   4140 B–1997 ...................   D6508–00(05) ..........   D6508, Rev. 2.54

66. Sulfide (as S), mg/L  .......    Sample Pretreatment .........................................    ..........................................    4500–S2¥ B, C–2000.

Titrimetric (iodine)  .......................................    ..........................................    4500–S2¥F–2000 ............     ..................................    I–3840–85.2 Colorimetric (methylene blue) .....................    ..........................................    4500–S2¥D–2000.

Ion Selective Electrode ...............................    ..........................................    4500–S2¥G–2000  ...........    D4658–08.

3

67. Sulfite (as SO3), mg/L ....    Titrimetric (iodine-iodate)  ...................................    ..........................................    4500–SO 2¥B–2000.

68. Surfactants, mg/L ...........   Colorimetric (methylene blue) ............................    ..........................................   5540 C–2000 ...................   D2330–02.

69. Temperature, C .............   Thermometric .....................................................    ..........................................   2550 B–2000 ...................    ..................................   See footnote.32

- Thallium–Total,4 mg/L ....   Digestion4, followed by any of the following:

AA direct aspiration .....................................    ..........................................   3111 B–1999.

AA furnace ..................................................   279.21(Issued 1978) ........   3113 B–2004.

STGFAA ......................................................   200.9, Rev. 2.2 (1994).

ICP/AES ......................................................   200.7, Rev. 4.4 (1994);

200.5 Rev. 4.2 (2003)68.

3120 B–1999 ...................   D1976–07.

19

ICP/MS ........................................................   200.8, Rev. 5.4 (1994)  ....   3125 B–2009 ...................   D5673–05 .................   993.143, I–4471–97.50

- Tin–Total,4 mg/L .............   Digestion4, followed by any of the following:.

AA direct aspiration .....................................    ..........................................   3111 B–1999 ...................    ..................................   I–3850–78.8 AA furnace ..................................................    ..........................................   3113 B–2004.

STGFAA ......................................................   200.9, Rev. 2.2 (1994).

ICP/AES ......................................................   200.5, Rev 4.2 (2003)68;

200.7, Rev. 4.4 (1994).

ICP/MS ........................................................   200.8, Rev. 5.4 (1994)  ....   3125 B–2009 ...................   D5673–05	993.14.3

- Titanium–Total,4 mg/L ....   Digestion4 followed by any of the following:

§ 136.3

AA direct aspiration .....................................    ..........................................   3111 D–1999. AA furnace ..................................................   283.21(Issued 1978).

ICP/AES ......................................................   200.7, Rev. 4.4 (1994).

ICP/MS ........................................................   200.8, Rev. 5.4 (1994)  ....   3125 B–2009 ...................   D5673–05	993.14.3

DCP .............................................................    ..........................................    ..........................................    ..................................   See footnote.34

20

§ 136.3

TABLE IB—LIST OF APPROVED INORGANIC TEST PROCEDURES—Continued

| Parameter | Methodology 58 | EPA 52 | Standard methods | ASTM | USGS/AOAC/Other |
| --- | --- | --- | --- | --- | --- |
| 73. Turbidity, NTU53 ............. | Nephelometric .................................................... | 180.1, Rev. 2.0 (1993) .... | 2130 B–2001 ................... | D1889–00 ................. | I–3860–85.2 |
|  |  |  |  |  | See footnote.65 |
|  |  |  |  |  | See footnote.66 |
|  |  |  |  |  | See footnote.67 |
| 74. Vanadium–Total,4 mg/L | Digestion4, followed by any of the following: |  |  |  |  |
|  | AA direct aspiration ..................................... | .......................................... | 3111 D–1999. |  |  |
|  | AA furnace .................................................. | .......................................... | 3113 B–2004 ................... | D3373–03(07). |  |
|  | ICP/AES ...................................................... | 200.5, Rev 4.2 (2003)68; | 3120 B–1999 ................... | D1976–07 ................. | I–4471–97.50 |
|  |  | 200.7, Rev. 4.4 (1994). |  |  |  |
|  | ICP/MS ........................................................ | 200.8, Rev. 5.4 (1994) .... | 3125 B–2009 ................... | D5673–05 ................. | 993.143, I–4020–05.70 |
|  | DCP ............................................................. | .......................................... | .......................................... | D4190–08 ................. | See footnote.34 |
|  | Colorimetric (Gallic Acid) ............................ | .......................................... | 3500–V B–1997. |  |  |
| 75. Zinc–Total4, mg/L ........... | Digestion4, followed by any of the following: |  |  |  |  |
|  | AA direct aspiration36 ................................. | .......................................... | 3111 B–1999 or 3111 C– | D1691–02(07) (A or | 974.273, p. 379, I–3900– |
|  |  |  | 1999. | B). | 85.2 |
|  | AA furnace .................................................. | 289.21(Issued 1978). |  |  |  |
|  | ICP/AES36 ................................................... | 200.5, Rev 4.2 (2003)68; | 3120 B–1999 ................... | D1976–07 ................. | I–4471–97.50 |
|  |  | 200.7, Rev. 4.4 (1994). |  |  |  |
|  | ICP/MS ........................................................ | 200.8, Rev. 5.4 (1994) .... | 3125 B–2009 ................... | D5673–05 ................. | 993.143, I–4020–05.70 |
|  | DCP36 ......................................................... | .......................................... | .......................................... | D4190–08 ................. | See footnote.34 |
|  | Colorimetric (Zincon) ................................... | .......................................... | 3500 Zn B–1997 .............. | .................................. | See footnote.33 |
| 76. Acid Mine Drainage ........ | ............................................................................. | 162769. |  |  |  |

Table IB Notes:

1 Methods for Chemical Analysis of Water and Wastes, EPA–600/4–79–020. Revised March 1983 and 1979, where applicable. U.S. EPA.

2 Methods for Analysis of Inorganic Substances in Water and Fluvial Sediments, Techniques of Water-Resource Investigations of the U.S. Geological Survey, Book 5, Chapter A1., unless otherwise stated. 1989. USGS.

3 Official Methods of Analysis of the Association of Official Analytical Chemists, Methods Manual, Sixteenth Edition, 4th Revision, 1998. AOAC International.

40 CFR Ch. I (7–1–17 Edition)

4 For the determination of total metals (which are equivalent to total recoverable metals) the sample is not filtered before processing. A digestion procedure is required to solubilize analytes in suspended material and to break down organic-metal complexes (to convert the analyte to a detectable form for colorimetric analysis). For non-platform graphite furnace atomic absorption determinations a digestion using nitric acid (as specified in Section 4.1.3 of Methods for the Chemical Analysis of Water and Wastes) is required prior to analysis. The procedure used should subject the sample to gentle, acid refluxing and at no time should the sample be taken to dryness. For direct aspiration flame atomic absorption determinations (FLAA) a com- bination acid (nitric and hydrochloric acids) digestion is preferred prior to analysis. The approved total recoverable digestion is described as Method 200.2 in Supplement I of ‘‘Methods for the Determination of Metals in Environmental Samples’’ EPA/600R–94/111, May, 1994, and is reproduced in EPA Methods 200.7, 200.8, and 200.9 from the same Supplement. However, when using the gaseous hydride technique or for the determination of certain elements such as antimony, arsenic, selenium, silver, and tin by non-EPA graphite furnace atomic absorption methods, mercury by cold vapor atomic absorption, the noble metals and titanium by FLAA, a specific or modified sample digestion procedure may be required and in all cases the ref- erenced method write-up should be consulted for specific instruction and/or cautions. For analyses using inductively coupled plasma-atomic emission spectrometry (ICP–AES), the direct cur- rent plasma (DCP) technique or the EPA spectrochemical techniques (platform furnace AA, ICP–AES, and ICP–MS) use EPA Method 200.2 or an approved alternate procedure (e.g., CEM microwave digestion, which may be used with certain analytes as indicated in Table IB); the total recoverable digestion procedures in EPA Methods 200.7, 200.8, and 200.9 may be used for those respective methods. Regardless of the digestion procedure, the results of the analysis after digestion procedure are reported as ‘‘total’’ metals.

5 Copper sulfate or other catalysts that have been found suitable may be used in place of mercuric sulfate.

6 Manual distillation is not required if comparability data on representative effluent samples are on file to show that this preliminary distillation step is not necessary: however, manual dis- tillation will be required to resolve any controversies. In general, the analytical method should be consulted regarding the need for distillation. If the method is not clear, the laboratory may compare a minimum of 9 different sample matrices to evaluate the need for distillation. For each matrix, a matrix spike and matrix spike duplicate are analyzed both with and without the dis- tillation step. (A total of 36 samples, assuming 9 matrices). If results are comparable, the laboratory may dispense with the distillation step for future analysis. Comparable is defined as

<20% RPD for all tested matrices). Alternatively the two populations of spike recovery percentages may be compared using a recognized statistical test.

7 Industrial Method Number 379–75 WE Ammonia, Automated Electrode Method, Technicon Auto Analyzer II. February 19, 1976. Bran & Luebbe Analyzing Technologies Inc.

8 The approved method is that cited in Methods for Determination of Inorganic Substances in Water and Fluvial Sediments, Techniques of Water-Resources Investigations of the U.S. Ge- ological Survey, Book 5, Chapter A1. 1979. USGS.

9 American National Standard on Photographic Processing Effluents. April 2, 1975. American National Standards Institute.

21

Environmental Protection Agency

10 In-Situ Method 1003–8–2009, Biochemical Oxygen Demand (BOD) Measurement by Optical Probe. 2009. In-Situ Incorporated.

11 The use of normal and differential pulse voltage ramps to increase sensitivity and resolution is acceptable.

12 Carbonaceous biochemical oxygen demand (CBOD5) must not be confused with the traditional BOD5 test method which measures ‘‘total BOD.’’ The addition of the nitrification inhibitor is not a procedural option, but must be included to report the CBOD5 parameter. A discharger whose permit requires reporting the traditional BOD5 may not use a nitrification inhibitor in the procedure for reporting the results. Only when a discharger’s permit specifically states CBOD5 is required can the permittee report data using a nitrification inhibitor.

13 OIC Chemical Oxygen Demand Method. 1978. Oceanography International Corporation.

14 Method 8000, Chemical Oxygen Demand, Hach Handbook of Water Analysis, 1979. Hach Company.

15 The back titration method will be used to resolve controversy.

16 Orion Research Instruction Manual, Residual Chlorine Electrode Model 97–70. 1977. Orion Research Incorporated. The calibration graph for the Orion residual chlorine method must be derived using a reagent blank and three standard solutions, containing 0.2, 1.0, and 5.0 mL 0.00281 N potassium iodate/100 mL solution, respectively.

17 Method 245.7, Mercury in Water by Cold Vapor Atomic Fluorescence Spectrometry, EPA–821–R–05–001. Revision 2.0, February 2005. US EPA.

18 National Council of the Paper Industry for Air and Stream Improvement (NCASI) Technical Bulletin 253, December 1971.

19 Method 8506, Biocinchoninate Method for Copper, Hach Handbook of Water Analysis. 1979. Hach Company.

20 When using a method with block digestion, this treatment is not required.

21 Industrial Method Number 378–75WA, Hydrogen ion (pH) Automated Electrode Method, Bran & Luebbe (Technicon) Autoanalyzer II. October 1976. Bran & Luebbe Analyzing Tech- nologies.

22 Method 8008, 1,10–Phenanthroline Method using FerroVer Iron Reagent for Water. 1980. Hach Company.

23 Method 8034, Periodate Oxidation Method for Manganese, Hach Handbook of Wastewater Analysis. 1979. Hach Company.

24 Methods for Analysis of Organic Substances in Water and Fluvial Sediments, Techniques of Water-Resources Investigations of the U.S. Geological Survey, Book 5, Chapter A3, (1972 Revised 1987) p. 14. 1987. USGS.

25 Method 8507, Nitrogen, Nitrite-Low Range, Diazotization Method for Water and Wastewater. 1979. Hach Company.

26 Just prior to distillation, adjust the sulfuric-acid-preserved sample to pH 4 with 1 + 9 NaOH.

27 The colorimetric reaction must be conducted at a pH of 10.0 0.2.

28 Addison, R.F., and R.G. Ackman. 1970. Direct Determination of Elemental Phosphorus by Gas–Liquid Chromatography, Journal of Chromatography, 47(3):421–426.

29 Approved methods for the analysis of silver in industrial wastewaters at concentrations of 1 mg/L and above are inadequate where silver exists as an inorganic halide. Silver halides such as the bromide and chloride are relatively insoluble in reagents such as nitric acid but are readily soluble in an aqueous buffer of sodium thiosulfate and sodium hydroxide to pH of 12. Therefore, for levels of silver above 1 mg/L, 20 mL of sample should be diluted to 100 mL by adding 40 mL each of 2 M Na2S2O3 and NaOH. Standards should be prepared in the same manner. For levels of silver below 1 mg/L the approved method is satisfactory.

30 The use of EDTA decreases method sensitivity. Analysts may omit EDTA or replace with another suitable complexing reagent provided that all method specified quality control accept- ance criteria are met.

31 For samples known or suspected to contain high levels of silver (e.g., in excess of 4 mg/L), cyanogen iodide should be used to keep the silver in solution for analysis. Prepare a cyan-

ogen iodide solution by adding 4.0 mL of concentrated NH4OH, 6.5 g of KCN, and 5.0 mL of a 1.0 N solution of I2 to 50 mL of reagent water in a volumetric flask and dilute to 100.0 mL. After digestion of the sample, adjust the pH of the digestate to >7 to prevent the formation of HCN under acidic conditions. Add 1 mL of the cyanogen iodide solution to the sample digestate and adjust the volume to 100 mL with reagent water (NOT acid). If cyanogen iodide is added to sample digestates, then silver standards must be prepared that contain cyanogen iodide as well. Prepare working standards by diluting a small volume of a silver stock solution with water and adjusting the pH7 with NH4OH. Add 1 mL of the cyanogen iodide solution and let stand 1 hour. Transfer to a 100-mL volumetric flask and dilute to volume with water.

32 ‘‘Water Temperature–Influential Factors, Field Measurement and Data Presentation,’’ Techniques of Water-Resources Investigations of the U.S. Geological Survey, Book 1, Chapter D1. 1975. USGS.

33 Method 8009, Zincon Method for Zinc, Hach Handbook of Water Analysis, 1979. Hach Company.

34 Method AES0029, Direct Current Plasma (DCP) Optical Emission Spectrometric Method for Trace Elemental Analysis of Water and Wastes. 1986–Revised 1991. Thermo Jarrell Ash Corporation.

35 In-Situ Method 1004–8–2009, Carbonaceous Biochemical Oxygen Demand (CBOD) Measurement by Optical Probe. 2009. In-Situ Incorporated.

36 Microwave-assisted digestion may be employed for this metal, when analyzed by this methodology. Closed Vessel Microwave Digestion of Wastewater Samples for Determination of Metals. April 16, 1992. CEM Corporation

37 When determining boron and silica, only plastic, PTFE, or quartz laboratory ware may be used from start until completion of analysis.

38 Only use n-hexane (n-Hexane—85% minimum purity, 99.0% min. saturated C6 isomers, residue less than 1 mg/L) extraction solvent when determining Oil and Grease parameters— Hexane Extractable Material (HEM), or Silica Gel Treated HEM (analogous to EPA Methods 1664 Rev. A and 1664 Rev. B). Use of other extraction solvents is prohibited.

39 Method PAI–DK01, Nitrogen, Total Kjeldahl, Block Digestion, Steam Distillation, Titrimetric Detection. Revised December 22, 1994. OI Analytical. 40 Method PAI–DK02, Nitrogen, Total Kjeldahl, Block Digestion, Steam Distillation, Colorimetric Detection. Revised December 22, 1994. OI Analytical. 41 Method PAI–DK03, Nitrogen, Total Kjeldahl, Block Digestion, Automated FIA Gas Diffusion. Revised December 22, 1994. OI Analytical.

§ 136.3

42 Method 1664 Rev. B is the revised version of EPA Method 1664 Rev. A. U.S. EPA. February 1999, Revision A. Method 1664, n-Hexane Extractable Material (HEM; Oil and Grease) and Silica Gel Treated n-Hexane Extractable Material (SGT–HEM; Non-polar Material) by Extraction and Gravimetry. EPA–821–R–98–002. U.S. EPA. February 2010, Revision B. Method 1664, n-Hexane Extractable Material (HEM; Oil and Grease) and Silica Gel Treated n-Hexane Extractable Material (SGT–HEM; Non-polar Material) by Extraction and Gravimetry. EPA–821– R–10–001.

43 Method 1631, Mercury in Water by Oxidation, Purge and Trap, and Cold Vapor Atomic Fluorescence Spectrometry, EPA–821–R–02–019. Revision E. August 2002, U.S. EPA. The ap- plication of clean techniques described in EPA’s Method 1669: Sampling Ambient Water for Trace Metals at EPA Water Quality Criteria Levels, EPA–821–R–96–011, are recommended to preclude contamination at low-level, trace metal determinations.

44 Method OIA–1677–09, Available Cyanide by Ligand Exchange and Flow Injection Analysis (FIA). 2010. OI Analytical.

22

§ 136.3

45 Open File Report 00–170, Methods of Analysis by the U.S. Geological Survey National Water Quality Laboratory—Determination of Ammonium Plus Organic Nitrogen by a Kjeldahl Di- gestion Method and an Automated Photometric Finish that Includes Digest Cleanup by Gas Diffusion. 2000. USGS.

46 Open File Report 93–449, Methods of Analysis by the U.S. Geological Survey National Water Quality Laboratory—Determination of Chromium in Water by Graphite Furnace Atomic Ab- sorption Spectrophotometry. 1993. USGS.

47 Open File Report 97–198, Methods of Analysis by the U.S. Geological Survey National Water Quality Laboratory—Determination of Molybdenum by Graphite Furnace Atomic Absorp- tion Spectrophotometry. 1997.. USGS.

48 Open File Report 92–146, Methods of Analysis by the U.S. Geological Survey National Water Quality Laboratory—Determination of Total Phosphorus by Kjeldahl Digestion Method and an Automated Colorimetric Finish That Includes Dialysis. 1992. USGS.

49 Open File Report 98–639, Methods of Analysis by the U.S. Geological Survey National Water Quality Laboratory—Determination of Arsenic and Selenium in Water and Sediment by Graphite Furnace-Atomic Absorption Spectrometry. 1999. USGS.

50 Open File Report 98–165, Methods of Analysis by the U.S. Geological Survey National Water Quality Laboratory—Determination of Elements in Whole-water Digests Using Inductively Coupled Plasma-Optical Emission Spectrometry and Inductively Coupled Plasma-Mass Spectrometry. 1998. USGS.

51 Open File Report 93–125, Methods of Analysis by the U.S. Geological Survey National Water Quality Laboratory—Determination of Inorganic and Organic Constituents in Water and Fluvial Sediments. 1993.. USGS.

52 Unless otherwise indicated, all EPA methods, excluding EPA Method 300.1–1, are published in U.S. EPA. May 1994. Methods for the Determination of Metals in Environmental Sam- ples, Supplement I, EPA/600/R–94/111; or U.S. EPA. August 1993. Methods for the Determination of Inorganic Substances in Environmental Samples, EPA/600/R–93/100. EPA Method

  - is US EPA. Revision 1.0, 1997, including errata cover sheet April 27, 1999. Determination of Inorganic Ions in Drinking Water by Ion Chromatography.

53 Styrene divinyl benzene beads (e.g., AMCO–AEPA–1 or equivalent) and stabilized formazin (e.g., Hach StablCal TM or equivalent) are acceptable substitutes for formazin.

54 Method D6508, Test Method for Determination of Dissolved Inorganic Anions in Aqueous Matrices Using Capillary Ion Electrophoresis and Chromate Electrolyte. December 2000. Waters Corp.

55 Kelada-01, Kelada Automated Test Methods for Total Cyanide, Acid Dissociable Cyanide, and Thiocyanate, EPA 821–B–01–009, Revision 1.2, August 2001. US EPA. Note: A 450–W UV lamp may be used in this method instead of the 550–W lamp specified if it provides performance within the quality control (QC) acceptance criteria of the method in a given instrument. Similarly, modified flow cell configurations and flow conditions may be used in the method, provided that the QC acceptance criteria are met.

56 QuikChem Method 10–204–00–1–X, Digestion and Distillation of Total Cyanide in Drinking and Wastewaters using MICRO DIST and Determination of Cyanide by Flow Injection Anal- ysis. Revision 2.2, March 2005. Lachat Instruments.

57 When using sulfide removal test procedures described in EPA Method 335.4–1, reconstitute particulate that is filtered with the sample prior to distillation.

58 Unless otherwise stated, if the language of this table specifies a sample digestion and/or distillation ‘‘followed by’’ analysis with a method, approved digestion and/or distillation are re- quired prior to analysis.

59 Samples analyzed for available cyanide using OI Analytical method OIA–1677–09 or ASTM method D6888–09 that contain particulate matter may be filtered only after the ligand ex- change reagents have been added to the samples, because the ligand exchange process converts complexes containing available cyanide to free cyanide, which is not removed by filtra- tion. Analysts are further cautioned to limit the time between the addition of the ligand exchange reagents and sample filtration to no more than 30 minutes to preclude settling of materials in samples.

40 CFR Ch. I (7–1–17 Edition)

60 Analysts should be aware that pH optima and chromophore absorption maxima might differ when phenol is replaced by a substituted phenol as the color reagent in Berthelot Reaction (‘‘phenol-hypochlorite reaction’’) colorimetric ammonium determination methods. For example when phenol is used as the color reagent, pH optimum and wavelength of maximum absorb- ance are about 11.5 and 635 nm, respectively—see, Patton, C.J. and S.R. Crouch. March 1977. Anal. Chem. 49:464–469. These reaction parameters increase to pH >12.6 and 665 nm when salicylate is used as the color reagent—see, Krom, M.D. April 1980. The Analyst 105:305–316.

61 If atomic absorption or ICP instrumentation is not available, the aluminon colorimetric method detailed in the 19th Edition of Standard Methods may be used. This method has poorer precision and bias than the methods of choice.

62 Easy (1–Reagent) Nitrate Method, Revision November 12, 2011. Craig Chinchilla.

63 Hach Method 10360, Luminescence Measurement of Dissolved Oxygen in Water and Wastewater and for Use in the Determination of BOD5 and cBOD5. Revision 1.2, October 2011. Hach Company. This method may be used to measure dissolved oxygen when performing the methods approved in Table IB for measurement of biochemical oxygen demand (BOD) and carbonaceous biochemical oxygen demand (CBOD).

64 In-Situ Method 1002–8–2009, Dissolved Oxygen (DO) Measurement by Optical Probe. 2009. In-Situ Incorporated. 65 Mitchell Method M5331, Determination of Turbidity by Nephelometry. Revision 1.0, July 31, 2008. Leck Mitchell.  66 Mitchell Method M5271, Determination of Turbidity by Nephelometry. Revision 1.0, July 31, 2008. Leck Mitchell.

67 Orion Method AQ4500, Determination of Turbidity by Nephelometry. Revision 5, March 12, 2009. Thermo Scientific.

68 EPA Method 200.5, Determination of Trace Elements in Drinking Water by Axially Viewed Inductively Coupled Plasma-Atomic Emission Spectrometry, EPA/600/R–06/115. Revision 4.2, October 2003. US EPA.

69 Method 1627, Kinetic Test Method for the Prediction of Mine Drainage Quality, EPA–821–R–09–002. December 2011. US EPA.

70 Techniques and Methods Book 5–B1, Determination of Elements in Natural-Water, Biota, Sediment and Soil Samples Using Collision/Reaction Cell Inductively Coupled Plasma-Mass Spectrometry, Chapter 1, Section B, Methods of the National Water Quality Laboratory, Book 5, Laboratory Analysis, 2006. USGS.

71 Water-Resources Investigations Report 01–4132, Methods of Analysis by the U.S. Geological Survey National Water Quality Laboratory—Determination of Organic Plus Inorganic Mer- cury in Filtered and Unfiltered Natural Water With Cold Vapor-Atomic Fluorescence Spectrometry, 2001. USGS.

#### Environmental Protection Agency	§ 136.3

TABLE IC—LIST OF APPROVED TEST PROCEDURES FOR NON-PESTICIDE ORGANIC COMPOUNDS

| Parameter 1 | Method | EPA 2 7 | Standard methods | ASTM | Other |
| --- | --- | --- | --- | --- | --- |
| 1. Acenaphthene .......................................... | GC ................. | 610. | 6410 B–2000 6440 B–2000 6410 B–2000 6440 B–2000 6410 B–2000 6440B–2000 .. 6200 C–1997. 6200 B–1997. ....................... 6410 B–2000. 6410 B–2000 6440 B–2000 6410 B–2000 6440 B–2000 6410 B–2000 6440 B–2000 6410 B–2000 6440 B–2000 6410 B–2000 6440 B–2000 ....................... ....................... 6410 B–2000 | ....................... D4657–92 (98). ....................... D4657–92 (98).. ....................... D4657–92 (98).. ....................... ....................... D4657–92 (98).. ....................... D4657–92 (98).. ....................... D4657–92 (98).. ....................... D4657–92 (98).. ....................... D4657–92 (98).. ....................... ....................... ....................... | See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 3, p.1. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 3, p. 130. See foot- note 6, p. S102. See foot- note 9, p. 27. |
| 2. Acenaphthylene ....................................... 3. Acrolein .................................................... 4. Acrylonitrile ............................................... 5. Anthracene ............................................... 6. Benzene ................................................... 7. Benzidine ................................................. 8. Benzo(a)anthracene ................................. 9. Benzo(a)pyrene ........................................ 10. Benzo(b)fluoranthene ............................. 11. Benzo(g,h,i)perylene .............................. 12. Benzo(k)fluoranthene ............................. 13. Benzyl chloride ....................................... 14. Butyl benzyl phthalate ............................ | GC/MS .......... HPLC ............ GC ................. GC/MS .......... HPLC ............ GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... HPLC ............ GC ................. GC/MS .......... Spectro-pho- tometric. GC/MS .......... HPLC ............ GC ................. GC/MS .......... HPLC ............ GC ................. GC/MS .......... HPLC ............ GC ................. GC/MS .......... HPLC ............ GC ................. GC/MS .......... HPLC ............ GC ................. GC/MS .......... HPLC ............ GC ................. GC/MS .......... GC ................. GC/MS .......... | 625, 1625B ... 610 ................ 610. 625, 1625B ... 610 ................ 603. 624 4, 1624B. 603. 624 4, 1624B. 610. 625, 1625B ... 610 ................ 602 ................ 624, 1624B ... ....................... 625 5, 1625B 605. 610. 625, 1625B ... 610 ................ 610. 625, 1625B ... 610 ................ 610. 625, 1625B ... 610 ................ 610. 625, 1625B ... 610 ................ 610. 625, 1625B ... 610 ................ ....................... ....................... 606. 625, 1625B ... |  |  |  |
| 15. bis(2-Chloroethoxy) methane ................. | GC ................. | 611. |  |  |  |

#### § 136.3

40 CFR Ch. I (7–1–17 Edition)

TABLE IC—LIST OF APPROVED TEST PROCEDURES FOR NON-PESTICIDE ORGANIC COMPOUNDS—

Continued

| Parameter 1 | Method | EPA 2 7 | Standard methods | ASTM | Other |
| --- | --- | --- | --- | --- | --- |
| 16. bis(2-Chloroethyl) ether ......................... 17. bis(2-Ethylhexyl) phthalate ..................... 18. Bromodichloromethane .......................... 19. Bromoform ............................................. 20. Bromomethane ....................................... 21. 4-Bromophenyl phenyl ether .................. 22. Carbon tetrachloride .............................. 23. 4-Chloro-3-methyl phenol ...................... 24. Chlorobenzene ....................................... 25. Chloroethane .......................................... 26. 2-Chloroethylvinyl ether ......................... 27. Chloroform ............................................. 28. Chloromethane ....................................... 29. 2-Chloronaphthalene .............................. 30. 2-Chlorophenol ....................................... 31. 4-Chlorophenyl phenyl ether .................. 32. Chrysene ................................................ 33. Dibenzo(a,h)anthracene ......................... | GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... HPLC ............ GC ................. GC/MS .......... | 625, 1625B ... 611. 625, 1625B ... 606. 625, 1625B ... 601 ................ 624, 1624B ... 601 ................ 624, 1624B ... 601 ................ 624, 1624B ... 611. 625, 1625B ... 601 ................ 624, 1624B ... 604 ................ 625, 1625B ... 601, 602 ........ 624, 1624B ... 601 ................ 624, 1624B ... 601. 624, 1624B. 601 ................ 624, 1624B ... 601 ................ 624, 1624B ... 612. 625, 1625B ... 604 ................ 625, 1625B ... 611. 625, 1625B ... 610. 625, 1625B ... 610 ................ 610. 625, 1625B ... | 6410 B–2000 6410 B–2000 6410 B–2000 6200 C–1997. 6200 B–1997. 6200 C–1997. 6200 B–1997. 6200 C–1997. 6200 B–1997. 6410 B–2000 6200 C–1997 6200 B–1997. 6420 B–2000. 6410 B–2000. 6200 C–1997 6200 B–1997. 6200 C–1997. 6200 B–1997. 6200 C–1997 6200 B–1997. 6200 C–1997. 6200 B–1997. 6410 B–2000 6420 B–2000. 6410 B–2000 6410 B–2000 6410 B–2000 6440 B–2000 6410 B–2000 | ....................... ....................... ....................... ....................... ....................... ....................... ....................... ....................... ....................... ....................... ....................... D4657–92 (98).. ....................... | See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 3, p. 130. See foot- note 9, p. 27. See foot- note 3, p. 130. See foot- note 3, p. 130. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. |
|  | HPLC ............ | 610 ................ | 6440 B–2000 | D4657–92 |  |
|  |  |  |  | (98).. |  |
| 34. Dibromochloromethane .......................... | GC ................. | 601 ................ | 6200 C–1997. |  |  |
|  | GC/MS .......... | 624, 1624B ... | 6200 B–1997. |  |  |
| 35. 1,2-Dichlorobenzene .............................. | GC ................. | 601, 602 ........ | 6200 C–1997. |  |  |

#### Environmental Protection Agency	§ 136.3

TABLE IC—LIST OF APPROVED TEST PROCEDURES FOR NON-PESTICIDE ORGANIC COMPOUNDS—

Continued

| Parameter 1 | Method | EPA 2 7 | Standard methods | ASTM | Other |
| --- | --- | --- | --- | --- | --- |
| 36. 1,3-Dichlorobenzene .............................. 37. 1,4-Dichlorobenzene .............................. 38. 3,3’-Dichlorobenzidine ............................ 39. Dichlorodifluoromethane ........................ 40. 1,1-Dichloroethane ................................. 41. 1,2-Dichloroethane ................................. 42. 1,1-Dichloroethene ................................. 43. trans-1,2-Dichloroethene ........................ 44. 2,4-Dichlorophenol ................................. 45. 1,2-Dichloropropane ............................... 46. cis-1,3-Dichloropropene ......................... 47. trans-1,3-Dichloropropene ..................... 48. Diethyl phthalate .................................... 49. 2,4-Dimethylphenol ................................ 50. Dimethyl phthalate ................................. 51. Di-n-butyl phthalate ................................ 52. Di-n-octyl phthalate ................................ 53. 2, 4-Dinitrophenol ................................... 54. 2,4-Dinitrotoluene ................................... 55. 2,6-Dinitrotoluene ................................... 56. Epichlorohydrin ...................................... | GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC/MS .......... HPLC ............ GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. | 624, 1625B ... 601, 602 ........ 624, 1625B ... 601, 602 ........ 624, 1625B ... 625, 1625B ... 605. 601. ....................... 601 ................ 624, 1624B ... 601 ................ 624, 1624B ... 601 ................ 624, 1624B ... 601 ................ 624, 1624B ... 604 ................ 625, 1625B ... 601 ................ 624, 1624B ... 601 ................ 624, 1624B ... 601 ................ 624, 1624B ... 606. 625, 1625B ... 604 ................ 625, 1625B ... 606. 625, 1625B ... 606. 625, 1625B ... 606. 625, 1625B ... 604 ................ 625, 1625B ... 609. 625, 1625B ... 609. 625, 1625B ... ....................... | 6200 B–1997 6200 C–1997. 6200 B–1997 6200 C–1997. 6200 B–1997 6410 B–2000. 6200 C–1997. 6200 C–1997. 6200 B–1997. 6200 C–1997. 6200 B–1997. 6200 C–1997. 6200 B–1997. 6200 C–1997. 6200 B–1997. 6420 B–2000. 6410 B–2000 6200 C–1997. 6200 B–1997. 6200 C–1997. 6200 B–1997. 6200 C–1997. 6200 B–1997. 6410 B–2000 6420 B–2000. 6410 B–2000 6410 B–2000 6410 B–2000 6410 B–2000 6420 B–2000 6410 B–2000. 6410 B–2000 6410 B–2000 ....................... | ....................... ....................... ....................... ....................... ....................... ....................... ....................... ....................... ....................... ....................... ....................... ....................... ....................... | See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 3, p. 130. |

#### § 136.3

40 CFR Ch. I (7–1–17 Edition)

TABLE IC—LIST OF APPROVED TEST PROCEDURES FOR NON-PESTICIDE ORGANIC COMPOUNDS—

Continued

| Parameter 1 | Method | EPA 2 7 | Standard methods | ASTM | Other |
| --- | --- | --- | --- | --- | --- |
| 57. Ethylbenzene ......................................... 58. Fluoranthene .......................................... 59. Fluorene ................................................. 1,2,3,4,6,7,8-Heptachloro-dibenzofuran 1,2,3,4,7,8,9-Heptachloro-dibenzofuran 1,2,3,4,6,7,8- Heptachloro-dibenzo-p- dioxin. 63. Hexachlorobenzene ............................... 64. Hexachlorobutadiene ............................. Hexachlorocyclopentadiene ................... 1,2,3,4,7,8-Hexachloro-dibenzofuran ..... 1,2,3,6,7,8-Hexachloro-dibenzofuran ..... 1,2,3,7,8,9-Hexachloro-dibenzofuran ..... 2,3,4,6,7,8-Hexachloro-dibenzofuran ..... 1,2,3,4,7,8-Hexachloro-dibenzo-p-dioxin 1,2,3,6,7,8-Hexachloro-dibenzo-p-dioxin 1,2,3,7,8,9-Hexachloro-dibenzo-p-dioxin 73. Hexachloroethane .................................. 74. Indeno(1,2,3-c,d) pyrene ........................ 75. Isophorone ............................................. 76. Methylene chloride ................................. 77. 2-Methyl-4,6-dinitrophenol ..................... 78. Naphthalene ........................................... 79. Nitrobenzene .......................................... | GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... HPLC ............ GC ................. GC/MS .......... HPLC ............ GC/MS .......... GC/MS .......... GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC/MS .......... GC/MS .......... GC/MS .......... GC/MS .......... GC/MS .......... GC/MS .......... GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... HPLC ............ GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... HPLC ............ GC ................. GC/MS .......... | ....................... 602 ................ 624, 1624B ... 610. 625, 1625B ... 610 ................ 610. 625, 1625B ... 610 ................ 1613B. 1613B. 1613B. 612. 625, 1625B ... 612. 625, 1625B ... 612. 625 5, 1625B 1613B. 1613B. 1613B. 1613B. 1613B. 1613B. 1613B. 612. 625, 1625B ... 610. 625, 1625B ... 610 ................ 609. 625, 1625B ... 601 ................ 624, 1624B ... 604 ................ 625, 1625B ... 610. 625, 1625B ... 610 ................ 609. 625, 1625B ... | ....................... 6200 C–1997. 6200 B–1997. 6410 B–2000 6440 B–2000 6410 B–2000 6440 B–2000 6410 B–2000 6410 B–2000 6410 B–2000 6410 B–2000 6410 B–2000 6440 B–2000 6410 B–2000 6200 C–1997. 6200 B–1997. 6420 B–2000. 6410 B–2000. 6410 B–2000. 6440 B–2000. 6410 B–2000 | ....................... ....................... D4657–92 (98).. ....................... D4657–92 (98).. ....................... ....................... ....................... ....................... ....................... D4657–92 (98).. ....................... ....................... ....................... ....................... ....................... | See foot- note 6, p. S102. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 3, p. 130. See foot- note 9, p. 27. See foot- note 9, p. 27 See foot- note 9, p. 27. |

#### Environmental Protection Agency	§ 136.3

TABLE IC—LIST OF APPROVED TEST PROCEDURES FOR NON-PESTICIDE ORGANIC COMPOUNDS—

Continued

| Parameter 1 | Method | EPA 2 7 | Standard methods | ASTM | Other |
| --- | --- | --- | --- | --- | --- |
| 80. 2-Nitrophenol .......................................... | HPLC ............ | ....................... | ....................... | D4657–92 | See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 3, p. 43; See footnote. 8 See foot- note 3, p. 43; See footnote. 8 See foot- note 3, p. 43; See footnote. 8 See foot- note 3, p. 43; See footnote. 8 See foot- note 3, p. 43; See footnote. 8 See foot- note 3, p. 43; See footnote. 8 See foot- note 3, p. 140. See foot- note 9, p. 27. |
|  |  |  |  | (98).. |  |
|  | GC ................. | 604 ................ | 6420 B–2000. |  |  |
| 81. 4-Nitrophenol .......................................... 82. N-Nitrosodimethylamine ......................... 83. N-Nitrosodi-n-propylamine ..................... 84. N-Nitrosodiphenylamine ......................... 85. Octachlorodibenzofuran ......................... Octachlorodibenzo-p-dioxin ................... 2,2’-Oxybis(2-chloro-propane) [also known as bis(2-Chloroisopropyl) ether]. 88. PCB–1016 .............................................. 89. PCB–1221 .............................................. 90. PCB–1232 .............................................. 91. PCB–1242 .............................................. 92. PCB–1248 .............................................. 93. PCB–1254 .............................................. 94. PCB–1260 .............................................. 1,2,3,7,8-Pentachloro-dibenzofuran ....... 2,3,4,7,8-Pentachloro-dibenzofuran ....... 1,2,3,7,8,-Pentachloro-dibenzo-p-dioxin 98. Pentachlorophenol ................................. | GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC/MS .......... GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC/MS .......... GC/MS .......... GC/MS .......... GC ................. GC/MS .......... | 625, 1625B ... 604 ................ 625, 1625B ... 607. 625 5, 1625B 607. 625 5, 1625B 607. 625 5, 1625B 1613B.10 1613B.10 611. 625, 1625B ... 608 ................ 625 ................ 608 ................ 625 ................ 608 ................ 625 ................ 608 ................ 625 ................ 608. 625 ................ 608 ................ 625 ................ 608 ................ 625 ................ 1613B. 1613B. 1613B. 604 ................ 625, 1625B ... | 6410 B–2000 6420 B–2000. 6410 B–2000 6410 B–2000 6410 B–2000 6410 B–2000 6410 B–2000 ....................... 6410 B–2000. ....................... 6410 B–2000. ....................... 6410 B–2000. ....................... 6410 B–2000. 6410 B–2000. ....................... 6410 B–2000. ....................... 6410 B–2000. 6420 B–2000 6410 B–2000 | ....................... ....................... ....................... ....................... ....................... ....................... ....................... ....................... ....................... ....................... ....................... ....................... ....................... ....................... |  |

#### § 136.3

40 CFR Ch. I (7–1–17 Edition)

TABLE IC—LIST OF APPROVED TEST PROCEDURES FOR NON-PESTICIDE ORGANIC COMPOUNDS—

Continued

| Parameter 1 | Method | EPA 2 7 | Standard methods | ASTM | Other |
| --- | --- | --- | --- | --- | --- |
| 99. Phenanthrene ......................................... | GC ................. | 610. | 6410 B–2000 6440 B–2000 6420 B–2000. 6410 B–2000 6410 B–2000 6440 B–2000 6200 C–1997 6200 B–1997. 6200 C–1997 6200 B–1997. 6200 C–1997. 6200 B–1997. ....................... 6410 B–2000 6200 C–1997. 6200 B–1997. 6200 C–1997. 6200 B–1997. 6200 C–1997. 6200 B–1997. 6200 C–1997. 6200 B–1997. 6420 B–2000. 6410 B–2000 | ....................... D4657–92 (98).. ....................... ....................... D4657–92 (98).. ....................... ....................... ....................... ....................... ....................... ....................... | See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 9, p. 27. See foot- note 3, p. 130. See foot- note 3, p. 130. See foot- note 3, p. 130. See foot- note 9, p. 27. See foot- note 3, p. 130. See foot- note 9, p. 27. |
| 100. Phenol .................................................. 101. Pyrene .................................................. 2,3,7,8-Tetrachloro-dibenzofuran ......... 2,3,7,8-Tetrachloro-dibenzo-p-dioxin ... 104. 1,1,2,2-Tetrachloroethane .................... 105. Tetrachloroethene ................................ 106. Toluene ................................................ 107. 1,2,4-Trichlorobenzene ........................ 108. 1,1,1-Trichloroethane ........................... 109. 1,1,2-Trichloroethane ........................... 110. Trichloroethene .................................... 111. Trichlorofluoromethane ........................ 112. 2,4,6-Trichlorophenol ........................... | GC/MS .......... HPLC ............ GC ................. GC/MS .......... GC ................. GC/MS .......... HPLC ............ GC/MS .......... GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... GC ................. GC/MS .......... | 625, 1625B ... 610 ................ 604 ................ 625, 1625B ... 610. 625, 1625B ... 610 ................ 1613B.10 613, 625 5a, 1613B. 601 ................ 624, 1624B ... 601 ................ 624, 1624B ... 602 ................ 624, 1624B ... 612 ................ 625, 1625B ... 601 ................ 624, 1624B ... 601 ................ 624, 1624B ... 601 ................ 624, 1624B ... 601 ................ 624 ................ 604 ................ 625, 1625B ... |  |  |  |
| 113. Vinyl chloride ........................................ | GC ................. | 601 ................ | 6200 C–1997. |  |  |
|  | GC/MS .......... | 624, 1624B ... | 6200 B–1997. |  |  |
| 114. Nonylphenol ......................................... | GC/MS .......... | ....................... | ....................... | D7065–06. |  |
| 115. Bisphenol A (BPA) ............................... | GC/MS .......... | ....................... | ....................... | D7065–06. |  |
| 116. p-tert-Octylphenol (OP) ........................ | GC/MS .......... | ....................... | ....................... | D7065–06. |  |
| 117. Nonylphenol Monoethoxylate (NP1EO) | GC/MS .......... | ....................... | ....................... | D7065–06. |  |
| 118. Nonylphenol Diethoxylate (NP2EO) .... | GC/MS .......... | ....................... | ....................... | D7065–06. |  |
| 119. Adsorbable Organic Halides (AOX) ..... | Adsorption | 1650.11 |  |  |  |
|  | and |  |  |  |  |
|  | Coulometric |  |  |  |  |
|  | Titration. |  |  |  |  |
| 120. Chlorinated Phenolics .......................... | In Situ | 1653.11 |  |  |  |
|  | Acetylation |  |  |  |  |
|  | and GC/MS. |  |  |  |  |

Table IC notes:

1 All parameters are expressed in micrograms per liter (g/L) except for Method 1613B, in which the parameters are expressed in picograms per liter (pg/L).

2 The full text of Methods 601–613, 624, 625, 1613B, 1624B, and 1625B are provided at Appendix A, Test Procedures for Analysis of Organic Pollutants, of this Part 136. The standardized test procedure to be used to determine the method detection limit (MDL) for these test procedures is given at Appendix B, Definition and Procedure for the Determination of the Method De- tection Limit, of this Part 136.

#### Environmental Protection Agency	§ 136.3

3 Methods for Benzidine: Chlorinated Organic Compounds, Pentachlorophenol and Pesticides in Water and Wastewater. Sep- tember 1978. U.S. EPA.

4 Method 624 may be used for quantitative determination of acrolein and acrylonitrile, provided that the laboratory has docu- mentation to substantiate the ability to detect and quantify these analytes at levels necessary to comply with any associated reg- ulations. In addition, the use of sample introduction techniques other than simple purge-and-trap may be required. QC accept- ance criteria from Method 603 should be used when analyzing samples for acrolein and acrylonitrile in the absence of such cri- teria in Method 624.

5 Method 625 may be extended to include benzidine, hexachlorocyclopentadiene, N-nitrosodimethylamine, N-nitrosodi-n-propyl- amine, and N-nitrosodiphenylamine. However, when they are known to be present, Methods 605, 607, and 612, or Method 1625B, are preferred methods for these compounds.

5a Method 625, screening only.

6 Selected Analytical Methods Approved and Cited by the United States Environmental Protection Agency, Supplement to the 15th Edition of Standard Methods for the Examination of Water and Wastewater. 1981. American Public Health Association (APHA).

7 Each analyst must make an initial, one-time demonstration of their ability to generate acceptable precision and accuracy with Methods 601–603, 624, 625, 1624B, and 1625B in accordance with procedures each in Section 8.2 of each of these Methods. Additionally, each laboratory, on an on-going basis must spike and analyze 10% (5% for Methods 624 and 625 and 100% for methods 1624B and 1625B) of all samples to monitor and evaluate laboratory data quality in accordance with Sections 8.3 and

8.4 of these methods. When the recovery of any parameter falls outside the warning limits, the analytical results for that param- eter in the unspiked sample are suspect. The results should be reported, but cannot be used to demonstrate regulatory compli- ance. These quality control requirements also apply to the Standard Methods, ASTM Methods, and other methods cited.

8 Organochlorine Pesticides and PCBs in Wastewater Using Empore TM Disk. Revised October 28, 1994. 3M Corporation.

9 Method O–3116–87 is in Open File Report 93–125, Methods of Analysis by U.S. Geological Survey National Water Quality Laboratory—Determination of Inorganic and Organic Constituents in Water and Fluvial Sediments. 1993. USGS.

10 Analysts may use Fluid Management Systems, Inc. Power-Prep system in place of manual cleanup provided the analyst meets the requirements of Method 1613B (as specified in Section 9 of the method) and permitting authorities. Method 1613, Re- vision B, Tetra- through Octa-Chlorinated Dioxins and Furans by Isotope Dilution HRGC/HRMS. Revision B, 1994. U.S. EPA. The full text of this method is provided in Appendix A to 40 CFR Part 136 and at http://water.epa.gov/scitech/methods/cwa/ index.cfm

11 Method 1650, Adsorbable Organic Halides by Adsorption and Coulometric Titration. Revision C, 1997. U.S. EPA. Method 1653, Chlorinated Phenolics in Wastewater by In Situ Acetylation and GCMS. Revision A, 1997. U.S. EPA. The full text for both of these methods is provided at appendix A in part 430, The Pulp, Paper, and Paperboard Point Source Category.

TABLE ID—LIST OF APPROVED TEST PROCEDURES FOR PESTICIDES 1

| Parameter | Method | EPA 2 7 10 | Standard methods | ASTM | Other |
| --- | --- | --- | --- | --- | --- |
| 1. Aldrin ................. 2. Ametryn ............. 3. Aminocarb ......... 4. Atraton ............... 5. Atrazine ............. 6. Azinphos methyl 7. Barban ............... 8. a-BHC ............... 9. b–BHC ............... 10. d-BHC .............. | GC ............................. GC/MS ....................... GC ............................. GC/MS ....................... TLC ............................ HPLC ......................... GC ............................. GC ............................. HPLC/MS ................... GC/MS ....................... GC ............................. GC-MS ....................... TLC ............................ HPLC ......................... GC ............................. GC/MS ....................... GC ............................. GC/MS ....................... GC ............................. | 608, 617 ................. 625 .......................... 507, 619 ................. 525.2 ....................... ................................. 632. 619 .......................... 507, 619 ................. ................................. 525.1, 525.2 ........... 614, 622, 1657 ....... ................................. ................................. 632. 608, 617 ................. 625 5 ....................... 608, 617 ................. 625 .......................... 608, 617 ................. | 6630 B– 2000 & C– 2000. 6410 B– 2000. ..................... ..................... ..................... ..................... ..................... ..................... ..................... ..................... ..................... ..................... 6630 B– 2000 & C– 2000. 6410 B– 2000. 6630 B– 2000 & C– 2000. 6410 B– 2000. 6630 B– 2000 & C– 2000. | D3086–90, D5812–96 (02). ..................... ..................... ..................... ..................... ..................... ..................... ..................... ..................... ..................... ..................... D3086–90, D5812– 96(02). ..................... D3086–90, D5812– 96(02). D3086–90, D5812– 96(02). | See footnote 3, p. 7; See footnote 4, O–3104–83; See footnote 8, 3M0222. See footnote 3, p. 83; See footnote 9, O–3106–93; See footnote 6, p. S68. See footnote 14, O–1121– 91. See footnote 3, p. 94; See footnote 6, p. S60. See footnote 3, p. 83; See footnote 6, p. S68. See footnote 3, p. 83; See footnote 6, p. S68; See footnote 9, O–3106–93. See footnote 12, O–2060– 01. See footnote 11, O–1126– 95. See footnote 3, p. 25; See footnote 6, p. S51. See footnote 11, O–1126– 95. See footnote 3, p. 104; See footnote 6, p. S64. See footnote 3, p. 7; See footnote 8, 3M0222. See footnote 11, O–1126– 95. See footnote 8, 3M0222. See footnote 8, 3M0222. |

#### § 136.3

40 CFR Ch. I (7–1–17 Edition)

TABLE ID—LIST OF APPROVED TEST PROCEDURES FOR PESTICIDES 1—Continued

| Parameter | Method | EPA 2 7 10 | Standard methods | ASTM | Other |
| --- | --- | --- | --- | --- | --- |
| 11. g-BHC (Lin- dane). 12. Captan ............. 13. Carbaryl ........... Carbo- phenothion. Chlordane ........ Chloropropham 17. 2,4-D ............... 18. 4,4’-DDD ......... 19. 4,4’-DDE .......... 20. 4,4’-DDT .......... Demeton-O ...... Demeton-S ...... 23. Diazinon .......... 24. Dicamba .......... Dichlofenthion Dichloran ......... 27. Dicofol ............. 28. Dieldrin ............ 29. Dioxathion ....... | GC/MS ....................... | 625 .......................... | 6410 B– | D3086–90, D5812– 96(02). ..................... D3086–90, D5812– 96(02). ..................... ..................... ..................... ..................... D3086–90, D5812– 96(02). ..................... ..................... ..................... D3086–90, D5812– 96(02). D3086–90, D5812– 96(02). ..................... D3086–90, D5812– 96(02). ..................... ..................... ..................... ..................... ..................... ..................... ..................... ..................... ..................... D3086–90, D5812– 96(02). ..................... ..................... | See footnote 3, p. 7; See footnote 4, O–3104–83; See footnote 8, 3M0222. See footnote 11, O–1126– 95. See footnote 3, p. 7. See footnote 3, p. 94, See footnote 6, p. S60. See footnote 12, O–2060– 01. See footnote 11, O–1126– 95. See footnote 4, page 27; See footnote 6, p. S73. See footnote 3, p. 7; See footnote 4, O–3104–83; See footnote 8, 3M0222. See footnote 3, p. 104; See footnote 6, p. S64. See footnote 3, p. 115; See footnote 4, O–3105–83. See footnote 12, O–2060– 01. See footnote 3, p. 7; See footnote 4, O–3105–83; See footnote 8, 3M0222. See footnote 3, p. 7; See footnote 4, O–3104–83; See footnote 8, 3M0222. See footnote 11, O–1126– 95. See footnote 3, p. 7; See footnote 4, O–3104–83; See footnote 8, 3M0222. See footnote 3, p. 25; See footnote 6, p. S51. See footnote 3, p. 25; See footnote 6, p. S51. See footnote 3, p. 25; See footnote 4, O–3104–83; See footnote 6, p. S51. See footnote 11, O–1126– 95. See footnote 3, p. 115. See footnote 12, O–2060– 01. See footnote 4, page 27; See footnote 6, p. S73. See footnote 3, p. 7; See footnote 4, O–3104–83. See footnote 3, p. 7; See footnote 4, O–3104–83; See footnote 8, 3M0222. See footnote 11, O–1126– 95. See footnote 4, page 27; See footnote 6, p. S73. |
|  |  |  | 2000. |  |  |
|  | GC ............................. GC/MS ....................... GC ............................. TLC ............................ HPLC ......................... HPLC/MS ................... GC/MS ....................... GC ............................. GC ............................. GC/MS ....................... TLC ............................ HPLC ......................... GC ............................. HPLC/MS ................... GC ............................. GC/MS ....................... GC ............................. GC/MS ....................... GC ............................. GC/MS ....................... GC ............................. GC ............................. GC ............................. GC/MS ....................... GC ............................. HPLC/MS ................... GC ............................. GC ............................. GC ............................. GC ............................. GC/MS ....................... GC ............................. | 608, 617 ................. 625 5 ....................... 617 .......................... ................................. 531.1, 632. 553 .......................... ................................. 617 .......................... 608, 617 ................. 625 .......................... ................................. 632. 615 .......................... ................................. 608, 617 ................. 625 .......................... 608, 617 ................. 625 .......................... 608, 617 ................. 625 .......................... 614, 622 ................. 614, 622 ................. 507, 614, 622, 1657 525.2 ....................... 615 .......................... ................................. 622.1 ....................... 608.2, 617 .............. 617 .......................... 608, 617 ................. 625 .......................... 614.1, 1657 ............ | 6630 B– 2000 & C– 2000. 6410 B– 2000. 6630 B– 2000. ..................... ..................... ..................... 6630 B– 2000. 6630 B– 2000 & C– 2000. 6410 B– 2000. ..................... 6640 B– 2001. ..................... 6630 B– 2000 & C– 2000. 6410 B– 2000. 6630 B– 2000 & C– 2000. 6410 B– 2000. 6630 B– 2000 & C– 2000. 6410 B– 2000. ..................... ..................... ..................... ..................... ..................... ..................... ..................... 6630 B– 2000. ..................... 6630 B– 2000 & C– 2000. 6410 B– 2000. ..................... |  |  |

#### Environmental Protection Agency	§ 136.3

TABLE ID—LIST OF APPROVED TEST PROCEDURES FOR PESTICIDES 1—Continued

| Parameter | Method | EPA 2 7 10 | Standard methods | ASTM | Other |
| --- | --- | --- | --- | --- | --- |
| 30. Disulfoton ........ 31. Diuron .............. Endosulfan I .... Endosulfan II ... Endosulfan Sul- fate. 35. Endrin .............. 36. Endrin aldehyde. 37. Ethion .............. 38. Fenuron ........... Fenuron-TCA .. Heptachlor ....... Heptachlor ep- oxide. 42. Isodrin ............. 43. Linuron ............ Malathion ......... Methiocarb ...... | GC ............................. GC/MS ....................... TLC ............................ HPLC ......................... HPLC/MS ................... GC ............................. GC/MS ....................... GC ............................. GC/MS ....................... GC ............................. GC/MS ....................... GC ............................. GC/MS ....................... GC ............................. GC/MS ....................... GC ............................. GC/MS ....................... TLC ............................ HPLC ......................... HPLC/MS ................... TLC ............................ HPLC ......................... GC ............................. GC/MS ....................... GC ............................. GC/MS ....................... GC ............................. GC ............................. HPLC ......................... HPLC/MS ................... GC/MS ....................... GC ............................. GC/MS ....................... TLC ............................ HPLC ......................... | 507, 614, 622, 1657 525.2 ....................... ................................. 632. 553 .......................... 608, 617 ................. 625 5 ....................... 608, 617 ................. 625 5 ....................... 608, 617 ................. 625 .......................... 505, 508, 608, 617, 1656. 525.1, 525.2, 625 5 608, 617 ................. 625. 614, 614.1,1657 ..... ................................. ................................. 632. ................................. ................................. 632. 505, 508, 608, 617, 1656. 525.1, 525.2, 625 ... 608, 617 ................. 625 .......................... 617 .......................... ................................. 632. 553 .......................... ................................. 614, 1657 ............... ................................. ................................. 632. | ..................... ..................... ..................... ..................... 6630 B– 2000 & C– 2000. 6410 B– 2000. 6630 B– 2000 & C– 2000. 6410 B– 2000. 6630 C– 2000. 6410 B– 2000. 6630 B– 2000 & C– 2000. 6410 B– 2000. 6630 C– 2000. ..................... ..................... ..................... ..................... ..................... 6630 B– 2000 & C– 2000. 6410 B– 2000. 6630 B– 2000 & C– 2000. 6410 B– 2000. 6630 B– 2000 & C– 2000. ..................... ..................... ..................... 6630 B– 2000. ..................... ..................... | ..................... ..................... ..................... ..................... D3086–90, D5812– 96(02). ..................... D3086–90, D5812– 96(02). ..................... ..................... D3086–90, D5812– 96(02). ..................... ..................... ..................... ..................... ..................... ..................... D3086–90, D5812– 96(02). D3086–90, D5812– 96(02). ..................... ..................... ..................... ..................... ..................... ..................... ..................... | See footnote 3, p. 25; See footnote 6 p. S51. See footnote 11, O–1126– 95. See footnote 3, p. 104; See footnote 6, p. S64. See footnote 12, O–2060– 01. See footnote 3, p. 7; See footnote 4, O–3104–83; See footnote 8, 3M022). See footnote 13, O–2002– 01. See footnote 3, p. 7; See footnote 8, 3M0222. See footnote 13, O–2002– 01. See footnote 8, 3M0222. See footnote 3, p. 7; See footnote 4, O–3104–83; See footnote 8, 3M0222. See footnote 8, 3M0222. See footnote 4, page 27; See footnote 6, p. S73. See footnote 13, O–2002– 01. See footnote 3, p. 104; See footnote 6, p. S64. See footnote 12, O–2060– 01. See footnote 3, p. 104; See footnote 6, p. S64. See footnote 3, p. 7; See footnote 4, O–3104–83; See footnote 8, 3M0222. See footnote 3, p. 7; See footnote 4, O–3104–83; See footnote 6, p. S73; See footnote 8, 3M0222. See footnote 4, O–3104–83; See footnote 6, p. S73. See footnote 3, p. 104; See footnote 6, p. S64. See footnote 12, O–2060– 01. See footnote 11, O–1126– 95. See footnote 3, p. 25; See footnote 6, p. S51. See footnote 11, O–1126– 95. See footnote 3, p. 94; See footnote 6, p. S60. |

#### § 136.3

40 CFR Ch. I (7–1–17 Edition)

TABLE ID—LIST OF APPROVED TEST PROCEDURES FOR PESTICIDES 1—Continued

| Parameter | Method | EPA 2 7 10 | Standard methods | ASTM | Other |
| --- | --- | --- | --- | --- | --- |
| Methoxychlor ... Mexacarbate ... 48. Mirex ............... 49. Monuron .......... 50. Monuron-TCA .. 51. Neburon .......... Parathion meth- yl. Parathion ethyl 54. PCNB .............. 55. Perthane .......... 56. Prometon ......... Prometryn ........ Propazine ........ 59. Propham .......... 60. Propoxur .......... 61. Secbumeton .... 62. Siduron ............ 63. Simazine ......... | HPLC/MS ................... GC ............................. GC/MS ....................... TLC ............................ HPLC ......................... GC ............................. TLC ............................ HPLC ......................... TLC ............................ HPLC ......................... TLC ............................ HPLC ......................... HPLC/MS ................... GC ............................. GC/MS ....................... GC ............................. GC/MS ....................... GC ............................. GC ............................. GC ............................. GC/MS ....................... GC ............................. GC/MS ....................... GC ............................. GC/MS ....................... TLC ............................ HPLC ......................... HPLC/MS ................... TLC ............................ HPLC ......................... TLC ............................ GC ............................. TLC ............................ HPLC ......................... HPLC/MS ................... GC ............................. | ................................. 505, 508, 608.2, 617, 1656. 525.1, 525.2 ........... ................................. 632. 617 .......................... ................................. 632. ................................. 632. ................................. 632. ................................. 614, 622, 1657 ....... ................................. 614 .......................... ................................. 608.1, 617 .............. 617 .......................... 507, 619 ................. 525.2 ....................... 507, 619 ................. 525.1, 525.2 ........... 507, 619, 1656 ....... 525.1, 525.2. ................................. 632. ................................. ................................. 632. ................................. 619. ................................. 632. ................................. 505, 507, 619, 1656 | ..................... 6630 B– 2000 & C– 2000. ..................... ..................... 6630 B– 2000 & C– 2000. ..................... ..................... ..................... ..................... 6630 B– 2000. ..................... 6630 B– 2000. ..................... 6630 B– 2000 & C– 2000. ..................... ..................... ..................... ..................... ..................... ..................... ..................... ..................... ..................... ..................... ..................... ..................... ..................... | ..................... D3086–90, D5812– 96(02). ..................... ..................... D3086–90, D5812– 96(02). ..................... ..................... ..................... ..................... ..................... ..................... ..................... ..................... D3086–90, D5812– 96(02). D3086–90, D5812– 96(02). ..................... ..................... ..................... ..................... ..................... ..................... ..................... ..................... ..................... ..................... ..................... ..................... | See footnote 12, O–2060– 01. See footnote 3, p. 7; See footnote 4, O–3104–83; See footnote 8, 3M0222. See footnote 11, O–1126– 95. See footnote 3, p. 94; See footnote 6, p.S60. See footnote 3, p. 7; See footnote 4, O–3104–83. See footnote 3, p. 104; See footnote 6, p. S64. See footnote 3, p. 104; See footnote 6, p. S64. See footnote 3, p. 104; See footnote 6, p. S64. See footnote 12, O–2060– 01. See footnote 4, page 27; See footnote 3, p. 25. See footnote 11, O–1126– 95. See footnote 4, page 27; See footnote 3, p. 25. See footnote 11, O–1126– 95. See footnote 3, p. 7. See footnote 4, O–3104–83. See footnote 3, p. 83; See footnote 6, p. S68; See footnote 9, O–3106–93. See footnote 11, O–1126– 95. See footnote 3, p. 83; See footnote 6, p. S68; See footnote 9,O–3106–93. See footnote 13, O–2002– 01. See footnote 3, p. 83; See footnote 6, p. S68; See footnote 9, O–3106–93. See footnote 3, p. 104; See footnote 6, p. S64. See footnote 12, O–2060– 01. See footnote 3, p. 94; See footnote 6, p. S60. See footnote 3, p. 83; See footnote 6, p. S68. See footnote 3, p. 104; See footnote 6, p. S64. See footnote 12, O–2060– 01. See footnote 3, p. 83; See footnote 6, p. S68; See footnote 9, O–3106–93. |

#### Environmental Protection Agency	§ 136.3

TABLE ID—LIST OF APPROVED TEST PROCEDURES FOR PESTICIDES 1—Continued

| Parameter | Method | EPA 2 7 10 | Standard methods | ASTM | Other |
| --- | --- | --- | --- | --- | --- |
| 64. Strobane .......... 65. Swep ............... 66. 2,4,5-T ............. 67. 2,4,5-TP (Silvex). Terbuthylazine Toxaphene ...... Trifluralin ......... | GC/MS ....................... GC ............................. TLC ............................ HPLC ......................... GC ............................. GC ............................. GC ............................. GC/MS ....................... GC ............................. GC/MS ....................... GC ............................. GC/MS ....................... | 525.1, 525.2 ........... 617 .......................... ................................. 632. 615 .......................... 615 .......................... 619, 1656 ............... ................................. 505, 508, 608, 617, 1656. 525.1, 525.2, 625 ... 508, 617, 627, 1656 525.2 ....................... | ..................... 6630 B– 2000 & C– 2000. ..................... 6640 B– 2001. 6640 B– 2001. ..................... ..................... 6630 B– 2000 & C– 2000. 6410 B– 2000. 6630 B– 2000. ..................... | ..................... ..................... ..................... ..................... ..................... ..................... ..................... D3086–90, D5812– 96(02). ..................... ..................... | See footnote 11, O–1126– 95. See footnote 3, p. 7. See footnote 3, p. 104; See footnote 6, p. S64. See footnote 3, p. 115; See footnote 4, O–3105–83. See footnote 3, p. 115; See footnote 4, O–3105–83. See footnote 3, p. 83; See footnote 6, p. S68. See footnote 13, O–2002– 01. See footnote 3, p. 7; See footnote 8; See footnote 4, O–3105–83. See footnote 3, p. 7; See footnote 9, O–3106–93. See footnote 11, O–1126– 95. |

Table ID notes:

1 Pesticides are listed in this table by common name for the convenience of the reader. Additional pesticides may be found under Table IC, where entries are listed by chemical name.

2 The standardized test procedure to be used to determine the method detection limit (MDL) for these test procedures is given at Appendix B, Definition and Procedure for the Determination of the Method Detection Limit, of this Part 136.

3 Methods for Benzidine, Chlorinated Organic Compounds, Pentachlorophenol and Pesticides in Water and Wastewater. Sep- tember 1978. U.S. EPA. This EPA publication includes thin-layer chromatography (TLC) methods.

4 Methods for the Determination of Organic Substances in Water and Fluvial Sediments, Techniques of Water-Resources In- vestigations of the U.S. Geological Survey, Book 5, Chapter A3. 1987. USGS.

5 The method may be extended to include a-BHC, g-BHC, endosulfan I, endosulfan II, and endrin. However, when they are known to exist, Method 608 is the preferred method.

6 Selected Analytical Methods Approved and Cited by the United States Environmental Protection Agency, Supplement to the 15th Edition of Standard Methods for the Examination of Water and Wastewater. 1981. American Public Health Association (APHA).

7 Each analyst must make an initial, one-time, demonstration of their ability to generate acceptable precision and accuracy with Methods 608 and 625 in accordance with procedures given in Section 8.2 of each of these methods. Additionally, each labora- tory, on an on-going basis, must spike and analyze 10% of all samples analyzed with Method 608 or 5% of all samples analyzed with Method 625 to monitor and evaluate laboratory data quality in accordance with Sections 8.3 and 8.4 of these methods. When the recovery of any parameter falls outside the warning limits, the analytical results for that parameter in the unspiked sample are suspect. The results should be reported, but cannot be used to demonstrate regulatory compliance. These quality control requirements also apply to the Standard Methods, ASTM Methods, and other methods cited.

8 Organochlorine Pesticides and PCBs in Wastewater Using Empore TM Disk. Revised October 28, 1994. 3M Corporation.

9 Method O–3106–93 is in Open File Report 94–37, Methods of Analysis by the U.S. Geological Survey National Water Quality Laboratory—Determination of Triazine and Other Nitrogen-Containing Compounds by Gas Chromatography With Nitrogen Phos- phorus Detectors. 1994. USGS.

10 EPA Methods 608.1, 608.2, 614, 614.1, 615, 617, 619, 622, 622.1, 627, and 632 are found in Methods for the Determination of Nonconventional Pesticides in Municipal and Industrial Wastewater, EPA 821–R–92–002, April 1992, U.S. EPA. The full text of Methods 608 and 625 are provided at Appendix A, Test Procedures for Analysis of Organic Pollutants, of this Part 136. EPA Methods 505, 507, 508, 525.1, 531.1 and 553 are in Methods for the Determination of Nonconventional Pesticides in Municipal and Industrial Wastewater, Volume II, EPA 821–R–93–010B, 1993, U.S. EPA. EPA Method 525.2 is in Determination of Organic Compounds in Drinking Water by Liquid-Solid Extraction and Capillary Column Gas Chromatography/Mass Spectrometry, Revi- sion 2.0, 1995, U.S. EPA. EPA methods 1656 and 1657 are in Methods For The Determination of Nonconventional Pesticides In Municipal and Industrial Wastewater, Volume I, EPA 821–R–93–010A, 1993, U.S. EPA.

11 Method O–1126–95 is in Open-File Report 95–181, Methods of Analysis by the U.S. Geological Survey National Water Quality Laboratory—Determination of pesticides in water by C–18 solid-phase extraction and capillary-column gas chroma- tography/mass spectrometry with selected-ion monitoring. 1995. USGS.

12 Method O–2060–01 is in Water-Resources Investigations Report 01–4134, Methods of Analysis by the U.S. Geological Sur- vey National Water Quality Laboratory—Determination of Pesticides in Water by Graphitized Carbon-Based Solid-Phase Extrac- tion and High-Performance Liquid Chromatography/Mass Spectrometry. 2001. USGS.

13 Method O–2002–01 is in Water-Resources Investigations Report 01–4098, Methods of Analysis by the U.S. Geological Sur- vey National Water Quality Laboratory—Determination of moderate-use pesticides in water by C–18 solid-phase extraction and capillary-column gas chromatography/mass spectrometry. 2001. USGS.

14 Method O–1121–91 is in Open-File Report 91–519, Methods of Analysis by the U.S. Geological Survey National Water Quality Laboratory—Determination of organonitrogen herbicides in water by solid-phase extraction and capillary-column gas chromatography/mass spectrometry with selected-ion monitoring. 1992. USGS.

34

§ 136.3

TABLE IE—LIST OF APPROVED RADIOLOGIC TEST TEST PROCEDURES

| Parameter and units | Method | Reference (method number or page) |
| --- | --- | --- |
|  |  | EPA 1 | Standard Methods 18th, 19th, 20th Ed. | Standard Methods On- line | ASTM | USGS 2 |
| Alpha-Total, pCi per liter .... Alpha-Counting error, pCi per liter. Beta-Total, pCi per liter ...... Beta-Counting error, pCi .... (a) Radium Total pCi per liter. (b) Ra, pCi per liter ................. | Proportional or scintillation counter. Proportional or scintillation counter. Proportional counter ............... Proportional counter ............... Proportional counter ............... Scintillation counter ................ | 900.0 .................. Appendix B ......... 900.0 .................. Appendix B ......... 903.0 .................. 903.1 .................. | 7110 B ......................... 7110 B ......................... 7110 B ......................... 7110 B ......................... 7500-Ra B .................... 7500-Ra C ................... | 7110 B–00 ................... 7110 B–00 ................... 7110 B–00 ................... 7110 B–00 ................... 7500-Ra B–01 .............. 7500-Ra C–01 ............. | D1943–90, 96 .............. D1943–90, 96 .............. D1890–90, 96 .............. D1890–90, 96 .............. D2460–90, 97. D3454–91, 97 .............. | pp. 75 and 78 3 p. 79 pp. 75 and 78 3 p. 79 p. 81 |

1 Prescribed Procedures for Measurement of Radioactivity in Drinking Water, EPA–600/4–80–032 (1980), U.S. Environmental Protection Agency, August 1980.

2 Fishman, M. J. and Brown, Eugene, ‘‘Selected Methods of the U.S. Geological Survey of Analysis of Wastewaters,’’ U.S. Geological Survey, Open-File Report 76–177 (1976).

40 CFR Ch. I (7–1–17 Edition)

3 The method found on p. 75 measures only the dissolved portion while the method on p. 78 measures only the suspended portion. Therefore, the two results must be added to obtain the ‘‘total.’’

#### Environmental Protection Agency	§ 136.3

TABLE IF—LIST OF APPROVED METHODS FOR PHARMACEUTICAL POLLUTANTS

| Pharmaceuticals pollutants | CAS registry No. | Analytical method number |
| --- | --- | --- |
| acetonitrile ................................................. | 75–05–8 ............................................. | 1666/1671/D3371/D3695. |
| n-amyl acetate ........................................... | 628–63–7 ........................................... | 1666/D3695. |
| n-amyl alcohol ........................................... | 71–41–0 ............................................. | 1666/D3695 |
| benzene ..................................................... | 71–43–2 ............................................. | D4763/D3695/502.2/524.2. |
| n-butyl-acetate ........................................... | 123–86–4 ........................................... | 1666/D3695. |
| tert-butyl alcohol ........................................ | 75–65–0 ............................................. | 1666. |
| chlorobenzene ........................................... | 108–90–7 ........................................... | 502.2/524.2. |
| chloroform .................................................. | 67–66–3 ............................................. | 502.2/524.2/551. |
| o-dichlorobenzene ..................................... | 95–50–1 ............................................. | 1625C/502.2/524.2. |
| 1,2-dichloroethane ..................................... | 107–06–2 ........................................... | D3695/502.2/524.2. |
| diethylamine ............................................... | 109–89–7 ........................................... | 1666/1671. |
| dimethyl sulfoxide ...................................... | 67–68–5 ............................................. | 1666/1671. |
| ethanol ....................................................... | 64–17–5 ............................................. | 1666/1671/D3695. |
| ethyl acetate .............................................. | 141–78–6 ........................................... | 1666/D3695. |
| n-heptane ................................................... | 142–82–5 ........................................... | 1666/D3695. |
| n-hexane .................................................... | 110–54–3 ........................................... | 1666/D3695. |
| isobutyraldehyde ........................................ | 78–84–2 ............................................. | 1666/1667. |
| isopropanol ................................................ | 67–63–0 ............................................. | 1666/D3695. |
| isopropyl acetate ....................................... | 108–21–4 ........................................... | 1666/D3695. |
| isopropyl ether ........................................... | 108–20–3 ........................................... | 1666/D3695. |
| methanol .................................................... | 67–56–1 ............................................. | 1666/1671/D3695. |
| Methyl Cellosolve D ................................... | 109–86–4 ........................................... | 1666/1671 |
| methylene chloride .................................... | 75–09–2 ............................................. | 502.2/524.2 |
| methyl formate ........................................... | 107–31–3 ........................................... | 1666. |
| 4-methyl-2-pentanone (MIBK) ................... | 108–10–1 ........................................... | 1624C/1666/D3695/D4763/524.2. |
| phenol ........................................................ | 108–95–2 ........................................... | D4763. |
| n-propanol ................................................. | 71–23–8 ............................................. | 1666/1671/D3695. |
| 2-propanone (acetone) .............................. | 67–64–1 ............................................. | D3695/D4763/524.2. |
| tetrahydrofuran .......................................... | 109–99–9 ........................................... | 1666/524.2. |
| toluene ....................................................... | 108–88–3 ........................................... | D3695/D4763/502.2/524.2. |
| triethlyamine .............................................. | 121–44–8 ........................................... | 1666/1671. |
| xylenes ...................................................... | (Note 1) ............................................. | 1624C/1666. |

Table 1F note:

1. 1624C: m-xylene 108–38–3, o,p-xylene E–14095 (Not a CAS number; this is the number provided in the Environmental Monitoring Methods Index (EMMI) database.); 1666: m,p-xylene 136777–61–2, o-xylene 95–47–6.

TABLE IG—TEST METHODS FOR PESTICIDE ACTIVE INGREDIENTS (40 CFR PART 455)

| EPA survey code | Pesticide name | CAS No. | EPA analytical method No.(s) 3 |
| --- | --- | --- | --- |
| 8 ........................... | Triadimefon .................................................. | 43121–43–3 | 507/633/525.1/525.2/1656 |
| 12 ......................... | Dichlorvos ..................................................... | 62–73–7 | 1657/507/622/525.1/525.2 |
| 16 ......................... | 2,4-D; 2,4-D Salts and Esters [2,4-Dichloro- | 94–75–7 | 1658/515.1/615/515.2/555 |
|  | phenoxyacetic acid]. |  |  |
| 17 ......................... | 2,4-DB; 2,4-DB Salts and Esters [2,4- | 94–82–6 | 1658/515.1/615/515.2/555 |
|  | Dichlorophenoxybutyric acid]. |  |  |
| 22 ......................... | Mevinphos .................................................... | 7786–34–7 | 1657/507/622/525.1/525.2 |
| 25 ......................... | Cyanazine .................................................... | 21725–46–2 | 629/507 |
| 26 ......................... | Propachlor .................................................... | 1918–16–7 | 1656/508/608.1/525.1/525.2 |
| 27 ......................... | MCPA; MCPA Salts and Esters [2-Methyl- | 94–74–6 | 1658/615/555 |
|  | 4-chlorophenoxyacetic acid]. |  |  |
| 30 ......................... | Dichlorprop; Dichlorprop Salts and Esters | 120–36–5 | 1658/515.1/615/515.2/555 |
|  | [2-(2,4-Dichlorophenoxy) propionic acid]. |  |  |
| 31 ......................... | MCPP; MCPP Salts and Esters [2-(2-Meth- | 93–65–2 | 1658/615/555 |
|  | yl-4-chlorophenoxy) propionic acid]. |  |  |
| 35 ......................... | TCMTB [2-(Thiocyanomethylthio) benzo-thi- | 21564–17–0 | 637 |
|  | azole]. |  |  |
| 39 ......................... | Pronamide .................................................... | 23950–58–5 | 525.1/525.2/507/633.1 |
| 41 ......................... | Propanil ........................................................ | 709–98–8 | 632.1/1656 |
| 45 ......................... | Metribuzin ..................................................... | 21087–64–9 | 507/633/525.1/525.2/1656 |
| 52 ......................... | Acephate ...................................................... | 30560–19–1 | 1656/1657 |
| 53 ......................... | Acifluorfen .................................................... | 50594–66–6 | 515.1/515.2/555 |
| 54 ......................... | Alachlor ........................................................ | 15972–60–8 | 505/507/645/525.1/525.2/1656 |
| 55 ......................... | Aldicarb ........................................................ | 116–06–3 | 531.1 |
| 58 ......................... | Ametryn ........................................................ | 834–12–8 | 507/619/525.2 |
| 60 ......................... | Atrazine ........................................................ | 1912–24–9 | 505/507/619/525.1/525.2/1656 |
| 62 ......................... | Benomyl ....................................................... | 17804–35–2 | 631 |
| 68 ......................... | Bromacil; Bromacil Salts and Esters ........... | 314–40–9 | 507/633/525.1/525.2/1656 |
| 69 ......................... | Bromoxynil .................................................... | 1689–84–5 | 1625/1661 |
| 69 ......................... | Bromoxynil octanoate ................................... | 1689–99–2 | 1656 |
| 70 ......................... | Butachlor ...................................................... | 23184–66–9 | 507/645/525.1/525.2/1656 |
| 73 ......................... | Captafol ........................................................ | 2425–06–1 | 1656 |

#### § 136.3

40 CFR Ch. I (7–1–17 Edition)

TABLE IG—TEST METHODS FOR PESTICIDE ACTIVE INGREDIENTS (40 CFR PART 455)—Continued

| EPA survey code | Pesticide name | CAS No. | EPA analytical method No.(s) 3 |
| --- | --- | --- | --- |
| 75 ......................... | Carbaryl [Sevin] ............................................ | 63–25–2 | 531.1/632/553 |
| 76 ......................... | Carbofuran ................................................... | 1563–66–2 | 531.1/632 |
| 80 ......................... | Chloroneb ..................................................... | 2675–77–6 | 1656/508/608.1/525.1/525.2 |
| 82 ......................... | Chlorothalonil ............................................... | 1897–45–6 | 508/608.2/525.1/525.2/1656 |
| 84 ......................... | Stirofos ......................................................... | 961–11–5 | 1657/507/622/525.1/525.2 |
| 86 ......................... | Chlorpyrifos .................................................. | 2921–88–2 | 1657/508/622 |
| 90 ......................... | Fenvalerate .................................................. | 51630–58–1 | 1660 |
| 103 ....................... | Diazinon ....................................................... | 333–41–5 | 1657/507/614/622/525.2 |
| 107 ....................... | Parathion methyl .......................................... | 298–00–0 | 1657/614/622 |
| 110 ....................... | DCPA [Dimethyl 2,3,5,6-tetrachloro- | 1861–32–1 | 508/608.2/525.1/525.2/515.1 2/515.2 2/1656 |
|  | terephthalate]. |  |  |
| 112 ....................... | Dinoseb ........................................................ | 88–85–7 | 1658/515.1/615/515.2/555 |
| 113 ....................... | Dioxathion .................................................... | 78–34–2 | 1657/614.1 |
| 118 ....................... | Nabonate [Disodium cyanodithio- | 138–93–2 | 630.1 |
|  | imidocarbonate]. |  |  |
| 119 ....................... | Diuron ........................................................... | 330–54–1 | 632/553 |
| 123 ....................... | Endothall ...................................................... | 145–73–3 | 548/548.1 |
| 124 ....................... | Endrin ........................................................... | 72–20–8 | 1656/505/508/608/617/525.1/525.2 |
| 125 ....................... | Ethalfluralin ................................................... | 55283–68–6 | 1656/627 See footnote 1 |
| 126 ....................... | Ethion ........................................................... | 563–12–2 | 1657/614/614.1 |
| 127 ....................... | Ethoprop ....................................................... | 13194–48–4 | 1657/507/622/525.1/525.2 |
| 132 ....................... | Fenarimol ..................................................... | 60168–88–9 | 507/633.1/525.1/525.2/1656 |
| 133 ....................... | Fenthion ....................................................... | 55–38–9 | 1657/622 |
| 138 ....................... | Glyphosate [N-(Phosphonomethyl) glycine] | 1071–83–6 | 547 |
| 140 ....................... | Heptachlor .................................................... | 76–44–8 | 1656/505/508/608/617/525.1/525.2 |
| 144 ....................... | Isopropalin .................................................... | 33820–53–0 | 1656/627 |
| 148 ....................... | Linuron ......................................................... | 330–55–2 | 553/632 |
| 150 ....................... | Malathion ...................................................... | 121–75–5 | 1657/614 |
| 154 ....................... | Methamidophos ............................................ | 10265–92–6 | 1657 |
| 156 ....................... | Methomyl ...................................................... | 16752–77–5 | 531.1/632 |
| 158 ....................... | Methoxychlor ................................................ | 72–43–5 | 1656/505/508/608.2/617/525.1/525.2 |
| 172 ....................... | Nabam .......................................................... | 142–59–6 | 630/630.1 |
| 173 ....................... | Naled ............................................................ | 300–76–5 | 1657/622 |
| 175 ....................... | Norflurazon ................................................... | 27314–13–2 | 507/645/525.1/525.2/1656 |
| 178 ....................... | Benfluralin .................................................... | 1861–40–1 | 1656/627 See footnote 1 |
| 182 ....................... | Fensulfothion ................................................ | 115–90–2 | 1657/622 |
| 183 ....................... | Disulfoton ..................................................... | 298–04–4 | 1657/507/614/622/525.2 |
| 185 ....................... | Phosmet ....................................................... | 732–11–6 | 1657/622.1 |
| 186 ....................... | Azinphos Methyl ........................................... | 86–50–0 | 1657/614/622 |
| 192 ....................... | Organo-tin pesticides ................................... | 12379–54–3 | Ind-01/200.7/200.9 |
| 197 ....................... | Bolstar .......................................................... | 35400–43–2 | 1657/622 |
| 203 ....................... | Parathion ...................................................... | 56–38–2 | 1657/614 |
| 204 ....................... | Pendimethalin ............................................... | 40487–42–1 | 1656 |
| 205 ....................... | Pentachloronitrobenzene ............................. | 82–68–8 | 1656/608.1/617 |
| 206 ....................... | Pentachlorophenol ....................................... | 87–86–5 | 625/1625/515.2/555/515.1/525.1/525.2 |
| 208 ....................... | Permethrin .................................................... | 52645–53–1 | 608.2/508/525.1/525.2/1656/1660 |
| 212 ....................... | Phorate ......................................................... | 298–02–2 | 1657/622 |
| 218 ....................... | Busan 85 [Potassium | 128–03–0 | 630/630.1 |
|  | dimethyldithiocarbamate]. |  |  |
| 219 ....................... | Busan 40 [Potassium N-hydroxymethyl-N- | 51026–28–9 | 630/630.1 |
|  | methyldithiocarbamate]. |  |  |
| 220 ....................... | KN Methyl [Potassium N-methyl- | 137–41–7 | 630/630.1 |
|  | dithiocarbamate]. |  |  |
| 223 ....................... | Prometon ...................................................... | 1610–18–0 | 507/619/525.2 |
| 224 ....................... | Prometryn ..................................................... | 7287–19–6 | 507/619/525.1/525.2 |
| 226 ....................... | Propazine ..................................................... | 139–40–2 | 507/619/525.1/525.2/1656 |
| 230 ....................... | Pyrethrin I ..................................................... | 121–21–1 | 1660 |
| 232 ....................... | Pyrethrin II .................................................... | 121–29–9 | 1660 |
| 236 ....................... | DEF [S,S,S-Tributyl phosphorotrithioate] ..... | 78–48–8 | 1657 |
| 239 ....................... | Simazine ....................................................... | 122–34–9 | 505/507/619/525.1/525.2/1656 |
| 241 ....................... | Carbam-S [Sodium dimethyldithio-carba- | 128–04–1 | 630/630.1 |
|  | mate]. |  |  |
| 243 ....................... | Vapam [Sodium methyldithiocarbamate] ..... | 137–42–8 | 630/630.1 |
| 252 ....................... | Tebuthiuron .................................................. | 34014–18–1 | 507/525.1/525.2 |
| 254 ....................... | Terbacil ......................................................... | 5902–51–2 | 507/633/525.1/525.2/1656 |
| 255 ....................... | Terbufos ....................................................... | 13071–79–9 | 1657/507/614.1/525.1/525.2 |
| 256 ....................... | Terbuthylazine .............................................. | 5915–41–3 | 619/1656 |
| 257 ....................... | Terbutryn ...................................................... | 886–50–0 | 507/619/525.1/525.2 |
| 259 ....................... | Dazomet ....................................................... | 533–74–4 | 630/630.1/1659 |
| 262 ....................... | Toxaphene ................................................... | 8001–35–2 | 1656/505/508/608/617/525.1/525.2 |
| 263 ....................... | Merphos [Tributyl phosphorotrithioate] ........ | 150–50–5 | 1657/507/525.1/525.2/622 |
| 264 ....................... | Trifluralin 1 .................................................... | 1582–09–8 | 1656/508/617/627/525.2 |

#### Environmental Protection Agency	§ 136.3

TABLE IG—TEST METHODS FOR PESTICIDE ACTIVE INGREDIENTS (40 CFR PART 455)—Continued

| EPA survey code | Pesticide name | CAS No. | EPA analytical method No.(s) 3 |
| --- | --- | --- | --- |
| 268 ....................... | Ziram [Zinc dimethyldithiocarbamate] .......... | 137–30–4 | 630/630.1 |

Table 1G notes:

1 Monitor and report as total Trifluralin.

2 Applicable to the analysis of DCPA degradates.

3 EPA Methods 608.1 through 645, 1645 through 1661, and Ind-01 are available in Methods For The Determination of Non- conventional Pesticides In Municipal and Industrial Wastewater, Volume I, EPA 821–R–93–010A, Revision I, August 1993, U.S. EPA. EPA Methods 200.9 and 505 through 555 are available in Methods For The Determination of Nonconventional Pesticides In Municipal and Industrial Wastewater, Volume II, EPA 821–R–93–010B, August 1993, U.S. EPA. The full text of Methods 608, 625 and 1625 are provided at Appendix A of this Part 136. The full text of Method 200.7 is provided at appendix C of this part 136.

38

§ 136.3

TABLE IH—LIST OF APPROVED MICROBIOLOGICAL METHODS FOR AMBIENT WATER

| Parameter and units | Method 1 | EPA | Standard methods | AOAC, ASTM, USGS | Other |
| --- | --- | --- | --- | --- | --- |
| Bacteria: Coliform (fecal), num- ber per 100 mL or number per gram dry weight. Coliform (fecal) in presence of chlorine, number per 100 mL. Coliform (total), num- ber per 100 mL. Coliform (total), in presence of chlorine, number per 100 mL. E. coli, number per 100 mL. Fecal streptococci, number per 100 mL. Enterococci, number per 100 mL. Protozoa: Cryptosporidium .......... 9. Giardia ........................ | Most Probable Number (MPN), 5 tube, 3 dilution, or. Membrane filter (MF) 2, sin- gle step. MPN, 5 tube, 3 dilution, or ... MF 2, single step 5 ................. MPN, 5 tube, 3 dilution, or ... MF 2, single step or two step MPN, 5 tube, 3 dilution, or ... MF 2 with enrichment ............ MPN 6 8 14, multiple tube, or Multiple tube/multiple well, or MF 2 5 6 7 8, two step, or ........ Single step ............................ MPN, 5 tube, 3 dilution, or ... MF 2, or ................................. Plate count ............................ MPN 6 8, multiple tube/mul- tiple well, or. MF 2 5 6 7 8 two step, or ......... Single step, or ....................... Plate count ............................ Filtration/IMS/FA ................... Filtration/IMS/FA ................... | p. 132 3 ............................. p. 124 3 ............................. p. 132 3 ............................. p. 124 3 ............................. p. 114 3 ............................. p. 108 3 ............................. p. 114 3 ............................. p. 111 3 ............................. .......................................... .......................................... 1103.1 19 .......................... 1603 20, 1604 21 ................ p. 139 3 ............................. p. 136 3 ............................. p. 143 3. .......................................... 1106.1 23 .......................... 1600 24 ............................. p. 143 3. 1622 25, 1623 26. 1623 26 | 9221 C E–2006. 9222 D–1997 9221 C E–2006. 9222 D–1997. 9221 B–2006. 9222 B–1997 ........................ 9221 B–2006. 9222 (B + B.5c)–1997. 9221 B.1–2006/9221 F– 2006 11 13. 9223 B–2004 12 ..................... 9222 B–1997/9222 G– 1997 18, 9213 D–2007. ............................................... 9230 B–2007. 9230 C–2007 ........................ ............................................... 9230 C–2007 ........................ 9230 C–2007. | B–0050–85 4 B–0025–85 4 991.15 10 ............................... D5392–93 9. ............................................... B–0055–85 4. D6503–99 9 ........................... D5259–92 9. | Colilert12 16, Colilert- 1812 15 16. mColiBlue-2417. Enterolert12 22. |

40 CFR Ch. I (7–1–17 Edition)

Table 1H notes:

1 The method must be specified when results are reported.

2 A 0.45-m membrane filter (MF) or other pore size certified by the manufacturer to fully retain organisms to be cultivated and to be free of extractables which could interfere with their growth.

3 Microbiological Methods for Monitoring the Environment, Water, and Wastes. EPA/600/8–78/017. 1978. US EPA.

4 U.S. Geological Survey Techniques of Water-Resource Investigations, Book 5, Laboratory Analysis, Chapter A4, Methods for Collection and Analysis of Aquatic Biological and Micro- biological Samples. 1989. USGS.

5 Because the MF technique usually yields low and variable recovery from chlorinated wastewaters, the Most Probable Number method will be required to resolve any controversies.

6 Tests must be conducted to provide organism enumeration (density). Select the appropriate configuration of tubes/filtrations and dilutions/volumes to account for the quality, character, consistency, and anticipated organism density of the water sample.

§ 136.3

39

Environmental Protection Agency

7 When the MF method has not been used previously to test waters with high turbidity, large numbers of noncoliform bacteria, or samples that may contain organisms stressed by chlorine, a parallel test should be conducted with a multiple-tube technique to demonstrate applicability and comparability of results.

8 To assess the comparability of results obtained with individual methods, it is suggested that side-by-side tests be conducted across seasons of the year with the water samples routinely tested in accordance with the most current Standard Methods for the Examination of Water and Wastewater or EPA alternate test procedure (ATP) guidelines.

9 Annual Book of ASTM Standards—Water and Environmental Technology. Section 11.02. 2000, 1999, 1996. ASTM International.

10 Official Methods of Analysis of AOAC International, 16th Edition, Volume I, Chapter 17. 1995. AOAC International.

11 The multiple-tube fermentation test is used in 9221B.1–2006. Lactose broth may be used in lieu of lauryl tryptose broth (LTB), if at least 25 parallel tests are conducted between this broth and LTB using the water samples normally tested, and this comparison demonstrates that the false-positive rate and false-negative rate for total coliform using lactose broth is less than 10 percent. No requirement exists to run the completed phase on 10 percent of all total coliform-positive tubes on a seasonal basis.

12 These tests are collectively known as defined enzyme substrate tests, where, for example, a substrate is used to detect the enzyme b-glucuronidase produced by E. coli.

13 After prior enrichment in a presumptive medium for total coliform using 9221B.1–2006, all presumptive tubes or bottles showing any amount of gas, growth or acidity within 48 h 3 h of incubation shall be submitted to 9221F–2006. Commercially available EC–MUG media or EC media supplemented in the laboratory with 50 g/mL of MUG may be used.

14 Samples shall be enumerated by the multiple-tube or multiple-well procedure. Using multiple-tube procedures, employ an appropriate tube and dilution configuration of the sample as needed and report the Most Probable Number (MPN). Samples tested with Colilertmay be enumerated with the multiple-well procedures, Quanti-Trayor Quanti-Tray/2000, and the MPN calculated from the table provided by the manufacturer.

15 Colilert-18is an optimized formulation of the Colilertfor the determination of total coliforms and E. coli that provides results within 18 h of incubation at 35 C, rather than the 24 h re- quired for the Colilerttest, and is recommended for marine water samples.

16 Descriptions of the Colilert, Colilert-18, Quanti-Tray, and Quanti-Tray/2000 may be obtained from IDEXX Laboratories Inc.

17 A description of the mColiBlue24test may be obtained from Hach Company.

18 Subject total coliform positive samples determined by 9222B–1997 or other membrane filter procedure to 9222G–1997 using NA–MUG media.

19 Method 1103.1: Escherichia coli (E. coli) in Water by Membrane Filtration Using membrane-Thermotolerant Escherichia coli Agar (mTEC), EPA–821–R–10–002. March 2010. US EPA.

20 Method 1603: Escherichia coli (E. coli) in Water by Membrane Filtration Using Modified membrane-Thermotolerant Escherichia coli Agar (Modified mTEC), EPA–821–R–09–007. De- cember 2009. US EPA.

21 Preparation and use of MI agar with a standard membrane filter procedure is set forth in the article, Brenner et al. 1993. New Medium for the Simultaneous Detection of Total Coliform and Escherichia coli in Water. Appl. Environ. Microbiol. 59:3534–3544 and in Method 1604: Total Coliforms and Escherichia coli (E. coli) in Water by Membrane Filtration by Using a Simul- taneous Detection Technique (MI Medium), EPA 821–R–02–024, September 2002, US EPA.

22 A description of the Enterolerttest may be obtained from IDEXX Laboratories Inc.

23 Method 1106.1: Enterococci in Water by Membrane Filtration Using membrane-Enterococcus-Esculin Iron Agar (mE–EIA), EPA–821–R–09–015. December 2009. US EPA.

24 Method 1600: Enterococci in Water by Membrane Filtration Using membrane-Enterococcus Indoxyl-b-D-Glucoside Agar (mEI), EPA–821–R–09–016. December 2009. US EPA.

25 Method 1622 uses a filtration, concentration, immunomagnetic separation of oocysts from captured material, immunofluorescence assay to determine concentrations, and confirmation through vital dye staining and differential interference contrast microscopy for the detection of Cryptosporidium. Method 1622: Cryptosporidium in Water by Filtration/IMS/FA, EPA–821–R– 05–001. December 2005. US EPA.

26 Method 1623 uses a filtration, concentration, immunomagnetic separation of oocysts and cysts from captured material, immunofluorescence assay to determine concentrations, and con- firmation through vital dye staining and differential interference contrast microscopy for the simultaneous detection of Cryptosporidium and Giardia oocysts and cysts. Method 1623. Cryptosporidium and Giardia in Water by Filtration/IMS/FA. EPA–821–R–05–002. December 2005. US EPA.

#### § 136.3

  - The documents required in this section are incorporated by reference into this section with approval of the Director of the Federal Register in ac- cordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies of the documents may be obtained from the sources listed in paragraph  (b)  of  this  section.  Docu- ments  may  be  inspected  at  EPA’s Water Docket, EPA West, 1301  Con- stitution  Avenue  NW.,  Room  B102, Washington, DC (Telephone: 202–566– 2426); or at the National Archives and Records Administration (NARA). For information on the availability of this material at NARA, call 202–741–6030.  These  test  proce- dures are incorporated as they exist on the day of approval and a notice of any change in these test procedures will be published  in  the  FEDERAL   REGISTER. The full texts of the methods from the following references which are cited in Tables IA, IB, IC, ID, IE, IF, IG and IH are incorporated by reference into this regulation and may be obtained from the source identified. All costs cited are  subject  to  change  and  must  be verified from the indicated source.

    - Environmental    Monitoring    and Support     Laboratory,     U.S.     Environ- mental   Protection   Agency,   Cincinnati OH    (US    EPA).    Available    at    http:// water.epa.gov/scitech/methods/cwa/ index.cfm  or  from:  National  Technical Information  Service,  5285  Port  Royal Road, Springfield, Virginia 22161

- Microbiological Methods for Moni- toring the Environment, Water, and Wastes. 1978. EPA/600/8–78/017, Pub. No. PB–290329/A.S.

- Part III Analytical Methodology, Section B Total Coliform Methods, page 108. Table IA, Note 3; Table IH, Note 3.

- Part III Analytical Methodology, Section B Total Coliform Methods, 2.6.2 Two-Step Enrichment Procedure, page

111. Table IA, Note 3; Table IH, Note 3.

- Part III Analytical Methodology, Section B Total Coliform Methods, 4 Most Probable Number (MPN) Method, page 114. Table IA, Note 3; Table IH, Note 3.

- Part III Analytical Methodology, Section   C   Fecal   Coliform   Methods,   2

#### 40 CFR Ch. I (7–1–17 Edition)

Direct Membrane Filter (MF) Method, page 124. Table IA, Note 3; Table IH, Note 3.

- Part III, Analytical Methodology, Section C Fecal Coliform Methods,  5 Most Probable Number (MPN) Method, page 132. Table IA, Note 3; Table IH, Note 3.

- Part III Analytical Methodology, Section D Fecal Streptococci, 2 Mem- brane Filter (MF) Method, page 136. Table IA, Note 3; Table IH, Note 3.

- Part III Analytical Methodology, Section D Fecal Streptococci, 4 Most Probable Number Method, page 139. Table IA, Note 3; Table IH, Note 3.

- Part III Analytical Methodology, Section D Fecal Streptococci, 5 Pour Plate Method, page 143. Table IA, Note 3; Table IH, Note 3.

- [Reserved]

    - Environmental   Monitoring   and Support    Laboratory,    U.S.    Environ- mental  Protection  Agency,  Cincinnati OH   (US   EPA).   Available   at   http:// water.epa.gov/scitech/methods/cwa/ index.cfm.

      - Method 300.1 (including Errata Cover Sheet, April 27, 1999), Determina- tion of Inorganic Ions in Drinking Water by Ion Chromatography,  Revi- sion 1.0, 1997. Table IB, Note 52.

      - Method 551, Determination of Chlorination Disinfection Byproducts and Chlorinated Solvents in Drinking Water by Liquid-Liquid Extraction and Gas Chromatography With Electron- Capture Detection. 1990. Table IF.

    - National    Exposure    Risk    Labora- tory-Cincinnati,        U.S.        Environmental Protection   Agency,   Cincinnati   OH   (US EPA).	Available	   or   from   the   National   Tech- nical  Information  Service  (NTIS),  5285 Port  Royal  Road,  Springfield,  VA  22161. Telephone: 800–553–6847.

      - Methods for the Determination of Inorganic  Substances   in   Environ- mental Samples. August 1993. EPA/600/ R–93/100, Pub. No. PB 94120821. Table IB, Note 52.

- Method 180.1, Determination of Turbidity  by  Nephelometry.  Revision

2.0. Table IB, Note 52.

- Method 300.0, Determination of Inorganic Anions by  Ion Chroma- tography. Revision 2.1. Table IB, Note 52.

#### Environmental Protection Agency	§ 136.3

- Method 335.4, Determination of Total Cyanide by Semi-Automated Col- orimetry. Revision 1.0. Table IB,  Notes 52 and 57.

- Method 350.1, Determination of Ammonium Nitrogen by Semi-Auto- mated Colorimetry. Revision 2.0. Table IB, Notes 30 and 52.

- Method 351.2, Determination of Total Kjeldahl Nitrogen by Semi-Auto- mated Colorimetry. Revision 2.0. Table IB, Note 52.

- Method 353.2, Determination of Nitrate-Nitrite Automated Colorim- etry. Revision 2.0. Table IB, Note 52.

- Method 365.1, Determination of Phosphorus by Automated  Colorim- etry. Revision 2.0. Table IB, Note 52.

- Method 375.2, Determination of Sulfate by Automated Colorimetry. Re- vision 2.0. Table IB, Note 52.

- Method 410.4, Determination of Chemical Oxygen Demand by Semi- Automated Colorimetry. Revision 2.0. Table IB, Note 52.

      - Methods for the Determination of Metals in Environmental Samples, Supplement I. May 1994. EPA/600/R–94/ 111, Pub. No. PB 95125472. Table IB, Note 52.

- Method 200.7, Determination of Metals and Trace Elements in Water and Wastes by Inductively Coupled Plasma-Atomic  Emission  Spectrom- etry. Revision 4.4. Table IB, Note 52.

- Method 200.8, Determination of Trace Elements in Water and  Wastes by Inductively Coupled Plasma Mass Spectrometry. Revision 5.3.  Table IB, Note 52.

- Method 200.9, Determination of Trace Elements by Stabilized Tempera- ture Graphite Furnace Atomic Absorp- tion Spectrometry. Revision 2.2. Table IB, Note 52.

- Method 218.6, Determination of Dissolved Hexavalent Chromium in Drinking Water, Groundwater, and In- dustrial Wastewater Effluents by Ion Chromatography. Revision 3.3. Table IB, Note 52.

- Method 245.1, Determination of Mercury in Water by Cold Vapor Atom- ic  Absorption  Spectrometry.  Revision

3.0. Table IB, Note 52.

    - National Exposure Risk Labora- tory-Cincinnati, U.S. Environmental Protection Agency, Cincinnati OH (US

EPA). Available at http://water.epa.gov/ scitech/methods/cwa/index.cfm.

- EPA Method 200.5, Determination of Trace Elements in Drinking  Water by Axially Viewed Inductively Coupled Plasma-Atomic  Emission  Spectrom- etry. Revision 4.2, October 2003. EPA/ 600/R–06/115. Table IB, Note 68.

- EPA Method 525.2, Determination of Organic Compounds in  Drinking Water by Liquid-Solid Extraction and Capillary Column Gas Chroma- tography/Mass Spectrometry. Revision 2.0, 1995. Table ID, Note 10.

    - Office of Research and Develop- ment,   Cincinnati   OH.   U.S.   Environ- mental  Protection  Agency,  Cincinnati OH   (US   EPA).   Available   at   http:// water.epa.gov/scitech/methods/cwa/ index.cfm  or  from  ORD  Publications, CERI,   U.S.   Environmental   Protection Agency, Cincinnati OH 45268.

- Methods	for	Benzidine, Chlorinated Organic Compounds, Pentachlorophenol, and Pesticides in Water and Wastewater. 1978. Table IC, Note 3; Table ID, Note 3.

- Methods for Chemical Analysis of Water and Wastes. March 1979. EPA– 600/4–79–020. Table IB, Note 1.

- Methods for  Chemical Analysis of Water and Wastes. Revised March 1983. EPA–600/4–79–020. Table IB, Note 1.

- Method 120.1, Conductance, Spe- cific Conductance, mhos at 25 C. Re- vision 1982. Table IB, Note 1.

- Method 130.1, Hardness, Total (mg/L as CaCO3), Colorimetric, Auto- mated EDTA. Issued 1971.  Table  IB, Note 1.

- Method 150.2, pH, Continuous Monitoring (Electrometric). December 1982. Table IB, Note 1.

- Method 160.4, Residue, Volatile, Gravimetric, Ignition at 550 C. Issued 1971. Table IB, Note 1.

- Method 206.5, Arsenic, Sample Di- gestion Prior to Total Arsenic Analysis by Silver Diethyldithiocarbamate or Hydride Procedures. Issued 1978. Table IB, Note 1.

- Method 231.2, Gold, Atomic Ab- sorption, Furnace Technique. Issued 1978. Table IB, Note 1.

- Method 245.2, Mercury, Auto- mated Cold Vapor Technique. Issued 1974. Table IB, Note 1.

#### § 136.3

- Method 252.2, Osmium, Atomic Absorption, Furnace Technique. Issued 1978. Table IB, Note 1.

- Method 253.2, Palladium, Atomic Absorption, Furnace Technique. Issued 1978. Table IB, Note 1.

- Method 255.2, Platinum, Atomic Absorption, Furnace Technique. Issued 1978. Table IB, Note 1.

- Method 265.2, Rhodium, Atomic Absorption, Furnace Technique. Issued 1978. Table IB, Note 1.

- Method 279.2, Thallium, Atomic Absorption, Furnace Technique. Issued 1978. Table IB, Note 1.

- Method 283.2, Titanium, Atomic Absorption, Furnace Technique. Issued 1978. Table IB, Note 1.

- Method 289.2, Zinc, Atomic Ab- sorption, Furnace Technique. Issued 1978. Table IB, Note 1.

- Method 310.2, Alkalinity, Colori- metric, Automated, Methyl Orange. Revision 1974. Table IB, Note 1.

- Method 351.1, Nitrogen, Kjeldahl, Total,	Colorimetric,	Automated Phenate. Revision 1978. Table IB, Note 1.

- Method 352.1, Nitrogen, Nitrate, Colorimetric, Brucine. Issued 1971. Table IB, Note 1.

- Method 365.3, Phosphorus, All Forms, Colorimetric, Ascorbic  Acid, Two Reagent. Issued 1978. Table IB, Note 1.

- Method 365.4, Phosphorus, Total, Colorimetric,  Automated,  Block Digestor AA II. Issued 1974. Table IB, Note 1.

- Method 410.3, Chemical Oxygen Demand, Titrimetric, High Level for Saline Waters. Revision 1978. Table IB, Note 1.

- Method 420.1, Phenolics, Total Recoverable,	Spectrophotometric, Manual 4–AAP With Distillation. Revi- sion 1978. Table IB, Note 1.

- Prescribed Procedures for Meas- urement of Radioactivity in Drinking Water. 1980. EPA–600/4–80–032. Table IE.

  - Method 900.0, Gross Alpha and Gross Beta Radioactivity. Table IE.

  - Method 903.0, Alpha-Emitting iRadio Isotopes. Table IE.

  - Method 903.1, Radium-226, Radon Emanation  Technique.  Table  IE.

  - Appendix B, Error and Statistical Calculations. Table IE.

#### 40 CFR Ch. I (7–1–17 Edition)

    - Office of Science and Technology,

U.S. Environmental Protection Agen- cy, Washington DC (US EPA). Avail- able at http://water.epa.gov/scitech/meth- ods/cwa/index.cfm.

- Method 1625C, Semivolatile Or- ganic Compounds by Isotope Dilution GCMS. 1989. Table IF.

- [Reserved]

    - Office   of   Water,   U.S.   Environ- mental  Protection  Agency,  Washington DC    (US    EPA).    Available    at    http:// water.epa.gov/scitech/methods/cwa/ index.cfm  or   from   National   Technical Information  Service,  5285  Port  Royal Road, Springfield, Virginia 22161.

- Method 1631, Mercury in Water by Oxidation, Purge and Trap, and Cold Vapor Atomic Fluorescence Spectrom- etry. Revision E, August 2002. EPA–821– R–02–019, Pub. No. PB2002–108220. Table IB, Note 43.

- Kelada-01, Kelada Automated Test Methods for Total Cyanide, Acid Dissociable Cyanide, and Thiocyanate. Revision 1.2, August 2001. EPA 821–B– 01–009, Pub. No. PB 2001–108275. Table IB, Note 55.

- In the compendium Analytical Methods for the Determination of Pollut- ants in Pharmaceutical Manufacturing Industry Wastewaters. July 1998. EPA 821–B–98–016, Pub. No. PB95201679. Table IF, Note 1.

- EPA Method 1666, Volatile Or- ganic Compounds Specific to the Phar- maceutical Industry by Isotope  Dilu- tion GC/MS. Table IF, Note 1.

- EPA Method 1667, Formaldehyde, Isobutyraldehyde, and Furfural by Derivatization Followed by High Per- formance Liquid Chromatography. Table IF.

- Method 1671, Volatile Organic Compounds Specific to the Pharma- ceutical Manufacturing Industry by GC/FID. Table IF.

- Methods For The Determination of Nonconventional Pesticides In Mu- nicipal and Industrial Wastewater, Vol- ume I. Revision I, August 1993. EPA 821–R–93–010A, Pub. No. PB 94121654. Tables ID, IG.

  - Method 608.1, Organochlorine Pes- ticides. Table ID, Note 10; Table IG, Note 3.

  - Method	608.2,	Certain Organochlorine Pesticides. Table  ID, Note 10; Table IG, Note 3.

#### Environmental Protection Agency	§ 136.3

  - Method 614, Organophosphorus Pesticides. Table ID, Note 10; Table IG, Note 3.

  - Method 614.1, Organophosphorus Pesticides. Table ID, Note 10; Table IG, Note 3.

  - Method 615, Chlorinated Herbi- cides. Table ID, Note 10; Table IG, Note 3.

  - Method 617, Organohalide Pes- ticides and PCBs. Table ID, Note 10; Table IG, Note 3.

  - Method 619, Triazine Pesticides. Table ID, Note 10; Table IG, Note 3.

  - Method 622, Organophosphorus Pesticides. Table ID, Note 10; Table IG, Note 3.

(I) Method 622.1, Thiophosphate Pes- ticides. Table ID, Note 10; Table IG, Note 3.

- Method 627, Dinitroaniline Pes- ticides. Table ID, Note 10; Table IG, Notes 1 and 3.

- Method 629, Cyanazine. Table IG, Note 3.

- Method 630, Dithiocarbamate Pes- ticides. Table IG, Note 3.

- Method 630.1, Dithiocarbamate Pesticides. Table IG, Note 3.

- Method 631, Benomyl and Carbendazim. Table IG, Note 3.

- Method 632, Carbamate and Urea Pesticides. Table ID, Note 10; Table IG, Note 3.

- Method 632.1, Carbamate and Amide Pesticides. Table IG, Note 3.

- Method 633, Organonitrogen Pes- ticides. Table IG, Note 3.

- Method 633.1, Neutral Nitrogen- Containing  Pesticides.  Table   IG,   Note 3.

- Method 637, MBTS and TCMTB. Table IG, Note 3.

- Method 644, Picloram. Table IG, Note 3.

- Method 645, Certain Amine Pes- ticides  and  Lethane.  Table  IG,  Note  3.

- Method 1656, Organohalide Pes- ticides. Table ID, Note 10; Table IG, Notes 1 and 3.

- Method 1657, Organophosphorus Pesticides. Table ID, Note 10; Table IG, Note 3.

- Method 1658, Phenoxy-Acid Herbi- cides. Table IG, Note 3.

- Method 1659, Dazomet. Table IG, Note 3.

- Method 1660, Pyrethrins and Pyrethroids. Table IG, Note 3.

(AA) Method 1661, Bromoxynil. Table IG, Note 3.

(BB) Ind-01. Methods EV–024 and EV– 025, Analytical Procedures for Deter- mining Total Tin and Triorganotin in Wastewater. Table IG, Note 3.

- Methods  For  The  Determination of Nonconventional Pesticides In Mu- nicipal and Industrial Wastewater, Vol- ume II. August 1993.  EPA 821–R–93– 010B, Pub. No. PB 94166311. Table IG.

  - Method 200.9, Determination of Trace Elements by Stabilized Tempera- ture Graphite Furnace Atomic Absorp- tion Spectrometry. Table IG, Note 3.

  - Method 505, Analysis of Organohalide Pesticides and Commer- cial Polychlorinated Biphenyl (PCB) Products in Water by Microextraction and Gas Chromatography. Table ID, Note 10; Table IG, Note 3.

  - Method 507, The Determination of Nitrogen- and Phosphorus-Containing Pesticides in Water by Gas Chroma- tography with a Nitrogen-Phosphorus Detector. Table ID, Note 10; Table IG, Note 3.

  - Method 508, Determination of Chlorinated Pesticides in Water by Gas Chromatography with an Electron Cap- ture Detector. Table ID, Note 10; Table IG, Note 3.

  - Method 515.1, Determination of Chlorinated Acids in Water by Gas Chromatography with an Electron Cap- ture Detector. Table IG, Notes 2 and 3.

  - Method 515.2, Determination of Chlorinated Acids in Water Using Liq- uid-Solid Extraction and Gas Chroma- tography with an Electron Capture De- tector. Table IG, Notes 2 and 3.

  - Method 525.1, Determination of Organic Compounds  in Drinking  Water by Liquids-Solid Extraction and Cap- illary Column Gas Chromatography/ Mass Spectrometry. Table ID, Note 10; Table IG, Note 3.

  - Method 531.1, Measurement of N- Methylcarbamoyloximes	and	N- Methylcarbamates in Water by Direct Aqueous Injection HPLC with Post- Column Derivatization. Table ID, Note 10; Table IG, Note 3.

  - Method 547, Determination of Glyphosate in Drinking Water by Di- rect-Aqueous-Injection HPLC, Post- Column Derivatization, and Fluores- cence Detection. Table IG, Note 3.

#### § 136.3

  - Method 548, Determination of Endothall in Drinking Water by Aque- ous Derivatization, Liquid-Solid Ex- traction, and Gas  Chromatography with Electron-Capture Detector. Table IG, Note 3.

  - Method 548.1, Determination of Endothall in Drinking Water by Ion- Exchange Extraction,  Acidic  Methanol Methylation and Gas Chromatography/ Mass Spectrometry. Table IG, Note 3.

  - Method 553, Determination of Benzidines and Nitrogen-Containing Pesticides in Water by Liquid-Liquid Extraction or Liquid-Solid Extraction and Reverse Phase High Performance Liquid Chromatography/Particle Beam/ Mass Spectrometry Table ID, Note 10; Table IG, Note 3.

  - Method 555, Determination of Chlorinated Acids in Water by High Performance Liquid Chromatography With a Photodiode Array Ultraviolet Detector. Table IG, Note 3.

- In the compendium Methods for the Determination of Organic Compounds in Drinking Water. Revised July 1991, December 1998. EPA–600/4–88–039, Pub. No. PB92–207703. Table IF.

  - EPA Method 502.2, Volatile Or- ganic Compounds in Water by Purge and Trap Capillary Column Gas Chro- matography with Photoionization and Electrolytic Conductivity Detectors in Series. Table IF.

  - [Reserved]

- In the compendium Methods for the Determination of  Organic  Compounds in Drinking Water-Supplement II. August 1992. EPA–600/R–92–129, Pub. No. PB92– 207703. Table IF.

- EPA Method 524.2, Measurement of Purgeable Organic Compounds in Water by Capillary Column Gas Chro- matography/Mass Spectrometry. Table IF.

- [Reserved]

- Methods for Measuring  the Acute Toxicity of Effluents and Re- ceiving Waters to Freshwater and Ma- rine Organisms, Fifth Edition. October 2002. EPA 821–R–02–012, Pub. No. PB2002–108488. Table IA, Note 26.

- Short-Term Methods for Meas- uring the Chronic Toxicity of Effluents and Receiving Waters to Freshwater Organisms, Fourth Edition. October 2002. EPA 821–R–02–013, Pub. No. PB2002–108489. Table IA, Note 27.

#### 40 CFR Ch. I (7–1–17 Edition)

- Short-Term Methods for Meas- uring the Chronic Toxicity of Effluents and Receiving Waters to Marine and Estuarine Organisms, Third Edition. October 2002. EPA 821–R–02–014, Pub. No. PB2002–108490. Table IA, Note 28.

    - Office   of   Water,   U.S.   Environ- mental Protection Agency, Washington DC    (US    EPA).    Available    at    http:// water.epa.gov/scitech/methods/cwa/ index.cfm.

- Method 245.7, Mercury in Water by Cold Vapor Atomic Fluorescence Spec- trometry. Revision 2.0, February 2005. EPA–821–R–05–001. Table IB, Note 17.

- Method 1103.1: Escherichia coli (E. coli) in Water by Membrane Filtration Using membrane-Thermotolerant Esch- erichia coli Agar (mTEC). March 2010. EPA–621–R–10–002. Table IH, Note 19.

- Method 1106.1: Enterococci in Water by Membrane Filtration Using membrane-Enterococcus-Esculin Iron Agar (mE–EIA). December 2009. EPA– 621–R–09–015. Table IH, Note 23.

- Method 1600: Enterococci in Water by Membrane Filtration Using membrane-Enterococcus Indoxyl-b-D- Glucoside Agar (mEI).  December 2009. EPA–821–R–09–016. Table IA, Note 25; Table IH, Note 24.

- Method 1603: Escherichia coli (E. coli) in Water by Membrane Filtration Using	Modified	membrane- Thermotolerant Escherichia coli Agar (Modified mTEC). December 2009. EPA– 821–R–09–007. Table IA, Note 22; Table IH, Note 20.

- Method 1604: Total Coliforms and Escherichia coli (E. coli) in Water by Membrane Filtration Using a Simulta- neous Detection Technique (MI Me- dium). September 2002. EPA–821–R–02–

024. Table IH, Note 21.

- Method 1622: Cryptosporidium in Water by Filtration/IMS/FA. December 2005. EPA–821–R–05–001. Table IH, Note 25.

- Method 1623: Cryptosporidium and Giardia in Water by Filtration/IMS/ FA. December 2005. EPA–821–R–05–002. Table IH, Note 26.

- Method 1627, Kinetic Test Method for the Prediction of Mine Drainage Quality. December 2011. EPA–821–R–09–

- Table IB, Note 69.

- Method 1664, n-Hexane Extract- able  Material  (HEM;  Oil  and  Grease)

#### Environmental Protection Agency	§ 136.3

and Silica Gel Treated n-Hexane Ex- tractable  Material  (SGT-HEM;  Non- polar Material) by Extraction and Gra- vimetry. Revision A, February 1999. EPA–821–R–98–002.  Table  IB,  Notes  38

and 42.

- Method 1664, n-Hexane Extract- able Material  (HEM;  Oil  and  Grease) and Silica Gel Treated n-Hexane Ex- tractable  Material  (SGT-HEM;  Non- polar Material) by Extraction and Gra- vimetry. Revision B, February 2010. EPA–821–R–10–001. Table IB, Notes 38 and 42.

- Method 1669, Sampling Ambient Water for Trace Metals at EPA Water Quality Criteria Levels.  July  1996. Table IB, Note 43.

- Method 1680:  Fecal  Coliforms  in Sewage Sludge (Biosolids) by Multiple- Tube Fermentation using  Lauryl Tryptose Broth (LTB) and EC Medium. April 2010. EPA–821–R–10–003. Table IA, Note 15.

- Method 1681: Fecal Coliforms in Sewage Sludge (Biosolids) by Multiple- Tube Fermentation using A–1 Medium. July 2006. EPA 821–R–06–013. Table IA, Note 20.

- Method 1682: Salmonella in Sew- age Sludge (Biosolids) by Modified Semisolid	Rappaport-Vassiliadis (MSRV) Medium. July 2006. EPA 821–R– 06–014. Table IA, Note 23.

    - American National Standards In- stitute, 1430 Broadway, New York NY 10018.

      - ANSI. American National Stand- ard on Photographic Processing Effluents. April 2, 1975. Table IB, Note 9.

      - [Reserved]

    - American Public Health Associa- tion, 1015 15th Street NW., Washington, DC 20005. Standard Methods Online is available through the Standard Meth- ods	Web	site	.

- Standard Methods for the Exam- ination of Water and Wastewater. 14th Edition, 1975. Table IB, Notes 17 and 27.

- Standard Methods for the Exam- ination of Water and Wastewater. 15th Edition, 1980, Table IB, Note 30; Table ID.

- Selected Analytical Methods Ap- proved and Cited by the United States Environmental Protection Agency, Supplement   to   the   15th   Edition   of

Standard Methods for the  Examination of Water and Wastewater. 1981. Table IC, Note 6; Table ID, Note 6.

- Standard Methods for the Exam- ination of Water and Wastewater. 18th Edition, 1992. Tables IA, IB, IC, ID,  IE, and IH.

- Standard Methods for the Exam- ination of Water and Wastewater. 19th Edition, 1995. Tables IA, IB, IC, ID,  IE, and IH.

- Standard Methods for the Exam- ination of Water and Wastewater. 20th Edition, 1998. Tables IA, IB, IC, ID,  IE, and IH.

- Standard Methods for the Exam- ination of Water and Wastewater. 21st Edition, 2005. Table IB, Notes 17 and 27.

- 2120, Color. 2001. Table IB.

- 2130, Turbidity. 2001. Table IB.

- 2310, Acidity. 1997. Table IB.

- 2320, Alkalinity. 1997. Table IB.

- 2340, Hardness. 1997. Table IB.

- 2510, Conductivity. 1997. Table IB.

- 2540, Solids. 1997. Table IB.

- 2550, Temperature. 2000. Table IB.

- 3111, Metals by Flame Atomic Absorption Spectrometry. 1999. Table IB.

- 3112, Metals by Cold-Vapor Atomic Absorption Spectrometry. 2009. Table  IB.

- 3113, Metals by Electrothermal Atomic Absorption Spectrometry. 2004. Table  IB.

- 3114, Arsenic and Selenium by Hydride Generation/Atomic Absorption Spectrometry. 2009. Table IB.

- 3120, Metals by Plasma Emission. 1999. Table IB.

- 3125, Metals by Inductively Cou- pled Plasma-Mass Spectrometry. 2009. Table  IB.

- 3500-Al, Aluminum. 2001. Table IB.

- 3500-As, Arsenic. 1997. Table IB.

- 3500-Ca, Calcium. 1997. Table IB.

- 3500-Cr, Chromium. 2009. Table IB.

- 3500-Cu, Copper. 1999. Table IB.

- 3500-Fe, Iron. 1997. Table IB.

- 3500-Pb, Lead. 1997. Table IB.

- 3500-Mn, Manganese. 1999. Table   IB.

#### § 136.3

- 3500-K, Potassium. 1997. Table IB.

- 3500-Na, Sodium. 1997. Table IB.

- 3500-V, Vanadium. 1997. Table IB.

- 3500-Zn, Zinc. 1997. Table IB.

- 4110, Determination of Anions by Ion Chromatography. 2000. Table IB.

- 4140, Inorganic Anions by Cap- illary Ion Electrophoresis. 1997. Table IB.

- 4500-B, Boron. 2000. Table IB.

- 4500-Cl¥, Chloride. 1997. Table  IB.

- 4500-Cl, Chlorine (Residual). 2000. Table IB.

- 4500-CN¥, Cyanide. 1999. Table IB.

(xl) 4500-F¥, Fluoride. 1997. Table IB. (xli) 4500-H + , pH Value. 2000. Table

IB.

(xlii) 4500-NH3, Nitrogen (Ammonia). 1997. Table IB.

#### 40 CFR Ch. I (7–1–17 Edition)

(lxii) 6630, Organochlorine Pesticides. 2000. Table ID.

(lxiii) 6640, Acidic Herbicide Com- pounds. 2001. Table ID.

(lxiv) 7110, Gross Alpha and Gross Beta Radioactivity (Total, Suspended, and Dissolved). 2000. Table IE.

(lxv) 7500, Radium. 2001. Table IE.

(lxvi) 9213, Recreational Waters. 2007. Table  IH.

(lxvii) 9221, Multiple-Tube Fermenta- tion Technique for Members of the Coliform Group. 2006. Table IA,  Notes 12 and 14; Table IH, Notes 11 and 13.

(lxviii) 9222, Membrane Filter Tech- nique for Members of the Coliform Group. 1997. Table IA; Table IH,  Note 18.

(lxix) 9223, Enzyme Substrate Coli- form Test. 2004. Table IA; Table IH.

(lxx) 9230, Fecal Enterococcus/Strepto- coccus Groups. 2007. Table IA; Table IH.

    - The Analyst, The Royal Society

2

(xliii)   4500-NO  ¥,  Nitrogen   (Nitrite). 2000. Table IB.

of  Chemistry,  RSC  Publishing,  Royal

Society of Chemistry, Thomas Graham

3

(xliv)   4500-NO ¥,  Nitrogen   (Nitrate). 2000. Table IB.

(xlv)   4500-Norg,   Nitrogen   (Organic). 1997. Table IB.

(xlvi)     4500-O,     Oxygen     (Dissolved). 2001. Table IB.

(xlvii) 4500-P, Phosphorus. 1999. Table IB.

(xlviii)  4500-SiO2,  Silica.  1997.  Table IB.

(xlix)  4500-S2¥,  Sulfide.  2000.   Table IB.

3

(l) 4500-SO 2¥, Sulfite. 2000. Table IB.

House,   Science   Park,   Milton   Road,

Cambridge CB4 0WF, United Kingdom. (Also available from most public li- braries.)

      - Spectrophotometric Determina- tion of Ammonia: A Study of a Modi- fied Berthelot Reaction Using Salicy- late  and  Dichloroisocyanurate.  Krom,

M.D. 105:305–316, April 1980. Table IB, Note 60.

      - [Reserved]

    - Analytical Chemistry, ACS Pub- lications,   1155   Sixteenth   St.   NW.,

4

(li)  4500-SO 2¥,  Sulfate.  1997.  Table IB.

(lii)   5210,   Biochemical   Oxygen   De- mand (BOD). 2001. Table IB.

(liii)  5220,  Chemical  Oxygen  Demand (COD). 1997. Table IB.

(liv)    5310,    Total    Organic    Carbon (TOC). 2000. Table IB.

(lv) 5520,  Oil  and Grease.  2001.  Table IB.

(lvi) 5530, Phenols. 2005. Table IB.

(lvii)  5540,  Surfactants.  2000.  Table IB.

(lviii)   6200,   Volatile   Organic   Com- pounds. 1997. Table IC.

(lix)  6410,  Extractable  Base/Neutrals and Acids. 2000. Tables IC, ID.

(lx) 6420, Phenols. 2000. Table IC.

(lxi)  6440,  Polynuclear  Aromatic  Hy- drocarbons. 2000. Table IC.

Washington   DC   20036.   (Also   available

from most public libraries.)

- Spectrophotometric and Kinetics Investigation of the Berthelot Reaction for the Determination of Ammonia. Patton, C.J. and S.R. Crouch. 49(3):464– 469, March 1977. Table IB, Note 60.

- [Reserved]

    - AOAC International, 481 North Frederick Avenue,  Suite 500,  Gaithers- burg, MD 20877–2417.

- Official Methods of Analysis of AOAC International. 16th Edition, 4th Revision, 1998.

- 920.203, Manganese in Water, Persulfate Method. Table IB, Note 3.

- 925.54, Sulfate in Water, Gravimetric  Method.  Table  IB,  Note  3.

- 973.40, Specific Conductance of Water. Table IB, Note 3.

#### Environmental Protection Agency	§ 136.3

- 973.41, pH of Water. Table IB, Note 3.

- 973.43, Alkalinity of Water, Titrimetric Method. Table IB, Note 3.

- 973.44, Biochemical Oxygen De- mand (BOD) of Water, Incubation Method. Table IB, Note 3.

- 973.45, Oxygen (Dissolved) in Water, Titrimetric Methods. Table IB, Note 3.

- 973.46, Chemical Oxygen Demand (COD) of Water, Titrimetric Methods. Table IB, Note 3.

- 973.47, Organic Carbon in Water, Infrared Analyzer Method. Table IB, Note 3.

- 973.48, Nitrogen (Total) in Water, Kjeldahl Method. Table IB, Note 3.

- 973.49, Nitrogen (Ammonia) in Water, Colorimetric Method. Table IB, Note 3.

- 973.50, Nitrogen (Nitrate) in Water, Brucine Colorimetric Method. Table IB, Note 3.

- 973.51, Chloride in Water, Mer- curic Nitrate Method. Table IB, Note 3.

- 973.52, Hardness of Water. Table IB, Note 3.

- 973.53, Potassium in Water, Atom- ic Absorption Spectrophotometric Method. Table IB, Note 3.

- 973.54, Sodium in Water, Atomic Absorption Spectrophotometric Meth- od. Table IB, Note 3.

- 973.55, Phosphorus in Water, Pho- tometric Method. Table IB, Note 3.

- 973.56, Phosphorus in Water, Automated Method. Table IB, Note 3.

- 974.27, Cadmium, Chromium, Cop- per, Iron, Lead, Magnesium, Man- ganese, Silver, Zinc in Water, Atomic Absorption Spectrophotometric Meth- od. Table IB, Note 3.

- 977.22, Mercury in Water, Flameless	Atomic	Absorption Spectrophotometric Method. Table IB, Note 3.

- 991.15. Total Coliforms and Esch- erichia coli in Water Defined  Substrate Technology (Colilert)   Method.  Table IA, Note 10; Table IH, Note 10.

- 993.14, Trace Elements in Waters and Wastewaters, Inductively Coupled Plasma-Mass Spectrometric Method. Table IB, Note 3.

- 993.23, Dissolved Hexavalent Chromium in Drinking Water, Ground Water,     and     Industrial     Wastewater

Effluents,  Ion  Chromatographic  Meth- od. Table IB, Note 3.

(X) 993.30, Inorganic Anions in Water, Ion  Chromatographic   Method.   Table IB, Note 3.

- [Reserved]

    - Applied and Environmental Microbiology, American Society for Microbiology, 1752 N Street NW., Wash- ington DC 20036. (Also available from most  public  libraries.)

- New Medium for the Simultaneous Detection of Total Coliforms and Esch- erichia coli in Water. Brenner, K.P., C.C. Rankin,  Y.R.  Roybal,  G.N.  Stelma,  Jr.,

P.V. Scarpino, and A.P. Dufour. 59:3534– 3544, November 1993. Table IH, Note 21.

- [Reserved]

    - ASTM International, 100 Barr Harbor Drive, P.O. Box C700, West Conshohocken, PA 19428–2959, or online.

- Annual Book of ASTM Standards, Water, and Environmental Technology, Section 11, Volumes 11.01 and 11.02. 1994.  Tables  IA,  IB,  IC,  ID,  IE,  and  IH.

- Annual Book of ASTM Standards, Water, and Environmental Technology, Section 11, Volumes 11.01 and 11.02. 1996.  Tables  IA,  IB,  IC,  ID,  IE,  and  IH.

- Annual Book of ASTM Stand- ards, Water, and Environmental Tech- nology, Section 11, Volumes 11.01 and

11.02. 1999. Tables IA, IB, IC, ID, IE, and IH.

- Annual Book of ASTM Stand- ards, Water, and Environmental Tech- nology, Section 11, Volumes 11.01 and

11.02. 2000. Tables IA, IB, IC, ID, IE, and IH.

- ASTM D511–08, Standard Test Methods for Calcium and  Magnesium in Water. November 2008. Table IB.

- ASTM D512–04, Standard Test Methods for Chloride Ion in Water. July 2004. Table IB.

- ASTM D515–88, Test Methods for Phosphorus in Water, March 1989. Table  IB.

- ASTM D516–07, Standard Test Method for Sulfate Ion in Water, Sep- tember 2007. Table IB.

- ASTM D858–07, Standard Test Methods for Manganese in Water. Au- gust 2007. Table IB.

- ASTM D859–05, Standard Test Method for Silica in Water. February 2005. Table IB.

#### § 136.3

- ASTM D888–09, Standard Test Methods for Dissolved Oxygen in Water. December 2009. Table IB.

- ASTM D1067–06, Standard Test Methods for Acidity or Alkalinity of Water. January 2007. Table IB.

- ASTM D1068–05e1, Standard Test Methods for Iron in Water. July 2005. Table  IB.

- ASTM D1125–95 (Reapproved 1999), Standard Test Methods for Elec- trical Conductivity and Resistivity of Water. December 1995. Table IB.

- ASTM D1126–02 (Reapproved 2007)e1, Standard Test Method for Hard- ness in Water. August 2007. Table IB.

- ASTM D1179–04, Standard Test Methods for Fluoride Ion in Water. July 2004. Table IB.

- ASTM D1246–05, Standard Test Method for Bromide Ion in Water. Feb- ruary 2005. Table IB.

- ASTM D1252–06, Standard Test Methods for Chemical Oxygen Demand (Dichromate  Oxygen  Demand)  of Water. February 2006. Table IB.

- ASTM D1253–08, Standard Test Method for Residual Chlorine in Water. October 2008. Table IB.

- ASTM D1293–99,  Standard  Test Methods for pH of Water. March 2000. Table   IB.

- ASTM D1426–08, Standard Test Methods for Ammonia Nitrogen in Water. September 2008. Table IB.

- ASTM D1687–02 (Reapproved 2007)e1, Standard Test Methods for Chromium in Water. August 2007. Table IB.

- ASTM D1688–07, Standard Test Methods for Copper in Water. August 2007. Table IB.

- ASTM D1691–02 (Reapproved 2007)e1, Standard Test Methods  for  Zinc in Water. August 2007. Table IB.

- ASTM D1783–01 (Reapproved 2007), Standard Test Methods for Phe- nolic Compounds in Water. January 2008). Table IB.

- ASTM D1886–08, Standard Test Methods for Nickel in Water. October 2008. Table IB.

- ASTM D1889–00, Standard Test Method for Turbidity of Water. October 2000. Table IB.

- ASTM D1890–96, Standard Test Method for Beta Particle Radioac- tivity of Water. April 1996. Table IE.

#### 40 CFR Ch. I (7–1–17 Edition)

- ASTM D1943–96, Standard Test Method for Alpha Particle Radioac- tivity of Water. April 1996. Table IE.

- ASTM D1976–07, Standard Test Method for Elements in Water by In- ductively-Coupled  Argon   Plasma Atomic Emission Spectroscopy. August 2007. Table IB.

- ASTM D2036–09, Standard Test Methods  for  Cyanides  in  Water.  Octo- ber 2009. Table IB.

- ASTM D2330–02, Standard Test Method for Methylene Blue Active Substances. August 2002. Table IB.

- ASTM D2460–97, Standard Test Method for Alpha-Particle-Emit- ting Isotopes of Radium in Water. Oc- tober 1997. Table IE.

- ASTM D2972–08, Standard Tests Method for Arsenic in Water. Oc- tober 2008. Table IB.

- ASTM D3223–02 (Reapproved 2007)e1, Standard Test Method for Total Mercury in Water. August 2007.  Table IB.

- ASTM D3371–95, Standard Test Method for Nitriles in Aqueous Solution by Gas-Liquid Chroma- tography, February 1996. Table IF.

- ASTM D3373–03 (Reapproved 2007)e1, Standard Test Method for Vana- dium in Water. September 2007.  Table IB.

- ASTM D3454–97, Standard Test Method for Radium-226 in Water. February 1998. Table IE.

- ASTM D3557–02 (Reapproved 2007)e1, Standard Test Method for Cad- mium in Water. September 2007.  Table IB.

(xl) ASTM D3558–08, Standard Test Method for Cobalt in Water. November 2008. Table IB.

(xli) ASTM D3559–08, Standard Test Methods for Lead in Water. October 2008. Table IB.

(xlii) ASTM D3590–02 (Reapproved 2006), Standard Test Methods for Total Kjeldahl Nitrogen in Water. February 2007. Table IB.

(xliii) ASTM D3645–08, Standard Test Methods for Beryllium in Water. Octo- ber 2008. Table IB.

(xliv) ASTM D3695–95, Standard Test Method for Volatile Alcohols in  Water by Direct Aqueous-Injection Gas Chro- matography. April 1995. Table IF.

#### Environmental Protection Agency	§ 136.3

(xlv) ASTM D3859–08, Standard Test Methods for Selenium in Water. Octo- ber 2008. Table IB.

(xlvi) ASTM D3867–04, Standard Test Method for Nitrite-Nitrate in  Water. July 2004. Table IB.

(xlvii) ASTM D4190–08, Standard Test Method for Elements in Water by Di- rect-Current Plasma Atomic Emission Spectroscopy. October 2008. Table IB.

(xlviii) ASTM  D4282–02,  Standard Test Method for Determination of Free Cyanide in Water and Wastewater by Microdiffusion. August 2002. Table IB.

(xlix) ASTM D4327–03, Standard Test Method for Anions in Water by Chemi- cally Suppressed Ion Chromatography. January 2003. Table IB.

(l) ASTM D4382–02 (Reapproved 2007)e1, Standard Test Method for Bar- ium in Water, Atomic Absorption Spectrophotometry, Graphite Furnace. September 2007. Table IB.

(li) ASTM D4657–92 (Reapproved 1998), Standard Test Method for Polynuclear Aromatic Hydrocarbons in Water. Jan- uary 1993. Table IC.

(lii) ASTM D4658–08, Standard Test Method for Sulfide Ion in Water. Au- gust 2008. Table IB.

(liii) ASTM D4763–88 (Reapproved 2001), Standard Practice for Identifica- tion of Chemicals in Water by Fluores- cence Spectroscopy. September 1988. Table   IF.

(liv) ASTM D4839–03, Standard Test Method for Total Carbon and Organic Carbon in Water by Ultraviolet, or Persulfate Oxidation, or Both, and In- frared Detection. January 2003. Table IB.

(lv) ASTM D5257–03, Standard Test Method for Dissolved Hexavalent Chro- mium in Water by Ion Chroma- tography. January 2003. Table IB.

(lvi) ASTM D5259–92, Standard Test Method for Isolation and  Enumeration of Enterococci from Water by the Membrane Filter Procedure. October 1992. Table IH, Note 9.

(lvii) ASTM D5392–93, Standard Test Method for Isolation and  Enumeration of Escherichia coli in Water by the Two- Step Membrane Filter Procedure. Sep- tember 1993. Table IH, Note 9.

(lviii) ASTM D5673–05, Standard Test Method for Elements in Water by In- ductively Coupled Plasma—Mass Spec- trometry. July 2005. Table IB.

(lix) ASTM D5907–03, Standard Test Method for Filterable and Nonfilter- able Matter in Water. July 2003. Table IB.

(lx) ASTM D6503–99, Standard Test Method for Enterococci in Water Using Enterolert. April 2000. Table IA Note 9, Table IH, Note 9.

(lxi)   ASTM.   D6508–00   (Reapproved 2005)E2, Standard Test Method for De- termination    of     Dissolved    Inorganic Anions in Aqueous Matrices Using Cap- illary   Ion   Electrophoresis   and   Chro- mate  Electrolyte.  April  2005.  Table  IB. (lxii) ASTM. D6888–09, Standard Test Method    for    Available    Cyanide    with Ligand  Displacement  and  Flow  Injec- tion  Analysis  (FIA)  Utilizing  Gas  Diffu- sion Separation and Amperometric De- tection. October 2009. Table IB, Note 59. (lxiii) ASTM. D6919–09, Standard Test Method for Determination of Dissolved Alkali  and  Alkaline  Earth  Cations  and Ammonium  in  Water  and  Wastewater by   Ion   Chromatography.   May   2009.

Table IB.

(lxiv) ASTM. D7065–06, Standard Test Method for Determination of Nonylphenol, Bisphenol A, p-tert- Octylphenol,	Nonylphenol Monoethoxylate and Nonylphenol Diethoxylate in Environmental Waters by Gas Chromatography Mass Spec- trometry. January 2007. Table IC.

(lxv) ASTM. D7237–10, Standard Test Method for Free Cyanide with Flow In- jection Analysis (FIA) Utilizing Gas Diffusion Separation and Ampero- metric Detection. June 2010. Table IB.

(lxvi) ASTM. D7284–08, Standard Test Method for Total Cyanide in Water by Micro Distillation followed by Flow In- jection Analysis with Gas Diffusion Separation and Amperometric Detec- tion. April 2008). Table IB.

(lxvii) ASTM. D7365–09a, Standard Practice  for  Sampling,  Preservation, and Mitigating Interferences in Water Samples for Analysis of Cyanide. Octo- ber 2009. Table II, Notes 5 and 6.

(lxviii) ASTM. D7511–09E2, Standard Test Method for Total Cyanide by Seg- mented Flow Injection Analysis, In- Line Ultraviolet Digestion and Amper- ometric Detection. March 2009. Table IB.

(lxix) ASTM. D7573–09, Standard Test Method for Total Carbon and Organic Carbon in Water by High Temperature

#### § 136.3

Catalytic  Combustion  and  Infrared  De- tection. November 2009. Table IB.

    - Bran & Luebbe Analyzing Tech- nologies, Inc., Elmsford NY 10523.

      - Industrial Method Number 378– 75WA, Hydrogen Ion (pH) Automated Electrode Method, Bran & Luebbe (Technicon) Auto Analyzer II. October 1976. Table IB, Note 21.

      - [Reserved]

    - CEM Corporation, P.O. Box 200, Matthews NC 28106–0200.

- Closed Vessel Microwave Diges- tion of Wastewater Samples for Deter- mination of Metals. April 16, 1992. Table IB, Note 36.

- [Reserved]

    - Craig R. Chinchilla, 900 Jorie Blvd., Suite 35, Oak Brook IL 60523. Telephone: 630–645–0600.

- Nitrate by Discrete Analysis Easy (1-Reagent) Nitrate Method, (Colori- metric, Automated, 1 Reagent).  Revi- sion 1, November 12, 2011. Table IB, Note 62.

- [Reserved]

    - Hach Company, P.O. Box 389, Loveland CO 80537.

- Method 8000, Chemical Oxygen De- mand. Hach Handbook of Water Anal- ysis. 1979. Table IB, Note 14.

- Method 8008, 1,10-Phenanthroline Method using  FerroVer  Iron  Reagent for Water. 1980. Table IB, Note 22.

- Method 8009, Zincon Method for Zinc. Hach Handbook  for  Water  Anal- ysis. 1979. Table IB, Note 33.

- Method 8034, Periodate Oxidation Method for Manganese. Hach Handbook for Water Analysis. 1979. Table IB, Note 23.

- Method 8506, Bicinchoninate Method for Copper. Hach Handbook of Water Analysis. 1979. Table IB, Note 19.

- Method 8507, Nitrogen, Nitrite— Low Range, Diazotization Method for Water and Wastewater. 1979. Table IB, Note 25.

- Hach Method 10360, Lumines- cence Measurement of  Dissolved  Oxy- gen in Water and Wastewater and for Use in the Determination of BOD5 and cBOD5. Revision 1.2,  October  2011. Table IB, Note 63.

- m-ColiBlue24Method, for  total Coliforms and E. coli. Revision 2,  1999. Table IA, Note 18; Table IH, Note  17.

    - IDEXX Laboratories  Inc.,  One Idexx Drive, Westbrook ME 04092.

#### 40 CFR Ch. I (7–1–17 Edition)

- ColilertMethod.  2002.   Table   IA, Notes  17  and  18;  Table  IH,  Notes  14, 15 and 16.

- Colilert-18Method.   2002.   Table IA, Notes 17 and 18; Table IH,  Notes 14, 15 and 16.

- EnterolertMethod. 2002.   Table IA, Note 24; Table IH, Note 12.

- Quanti-TrayMethod. 2002.  Table IA, Note 18; Table IH, Notes 14  and 16.

- Quanti-Tray/2000   Method.    2002. Table IA,  Note  18;  Table  IH,   Notes 14 and 16.

    - In-Situ Incorporated, 221 E. Lin- coln Ave., Ft. Collins CO 80524. Tele- phone: 970–498–1500.

      - In-Situ Inc. Method 1002–8–2009, Dissolved Oxygen Measurement by Op- tical Probe. 2009. Table IB, Note 64.

      - In-Situ Inc. Method 1003–8–2009, Biochemical Oxygen Demand (BOD) Measurement by Optical Probe. 2009. Table IB, Note 10.

      - In-Situ Inc. Method 1004–8–2009, Carbonaceous Biochemical Oxygen De- mand (CBOD) Measurement by Optical Probe. 2009. Table IB, Note 35.

    - Journal of Chromatography, Elsevier/North-Holland, Inc., Journal Information Centre, 52 Vanderbilt Ave- nue, New York NY 10164. (Also avail- able from most public libraries.

- Direct Determination  of  Ele- mental Phosphorus by Gas-Liquid Chromatography.  Addison,   R.F.   and R.G. Ackman. 47(3): 421–426, 1970. Table IB, Note 28.

- [Reserved]

    - Lachat Instruments, 6645 W. Mill Road, Milwaukee WI 53218, Telephone: 414–358–4200.

      - QuikChem Method 10–204–00–1–X, Digestion and Distillation of Total Cy- anide in Drinking and Wastewaters using MICRO DIST and  Determination of Cyanide by Flow Injection Analysis. Revision 2.2, March 2005. Table IB, Note 56.

      - [Reserved]

    - Leck Mitchell, Ph.D., P.E., 656 Independence Valley Dr., Grand Junc- tion CO 81507. Telephone: 970–244–8661.

      - Mitchell Method M5271, Deter- mination	of	Turbidity	by Nephelometry. Revision 1.0, July 31, 2008. Table IB, Note 66.

      - Mitchell Method M5331, Deter- mination	of	Turbidity	by

#### Environmental Protection Agency	§ 136.3

Nephelometry.   Revision   1.0,   July   31,

2008. Table IB, Note 65.

    - National Council of the Paper In- dustry for Air and Stream Improve- ments, Inc. (NCASI), 260 Madison Ave- nue, New York NY 10016.

- NCASI Technical Bulletin No. 253, An Investigation of Improved Proce- dures for Measurement of Mill Effluent and Receiving Water Color. December 1971. Table IB, Note 18.

- [Reserved]

    - Oceanography International Cor- poration, 512 West Loop, P.O. Box 2980, College Station TX 77840.

      - OIC Chemical Oxygen Demand Method. 1978. Table IB, Note 13.

      - [Reserved]

    - OI Analytical, Box 9010, College Station TX 77820–9010.

- Method OIA–1677–09, Available Cy- anide by Ligand Exchange and Flow In- jection Analysis (FIA). Copyright 2010. Table IB, Note 59.

- Method PAI–DK01, Nitrogen, Total Kjeldahl, Block Digestion, Steam Distillation, Titrimetric Detection. Re- vised December 22, 1994. Table IB, Note 39.

- Method PAI–DK02, Nitrogen, Total Kjeldahl, Block Digestion, Steam Distillation, Colorimetric Detection. Revised December 22, 1994. Table IB, Note 40.

- Method PAI–DK03, Nitrogen, Total Kjeldahl, Block Digestion, Auto- mated FIA Gas Diffusion. Revised De- cember 22, 1994. Table IB, Note 41.

    - ORION Research Corporation, 840 Memorial Drive, Cambridge, Massachu- setts 02138.

- ORION Research Instruction Man- ual, Residual Chlorine Electrode Model 97–70. 1977. Table IB, Note 16.

- [Reserved]

    - Technicon Industrial Systems, Tarrytown NY 10591.

- Industrial Method Number 379– 75WE Ammonia, Automated Electrode Method, Technicon Auto Analyzer II. February 19, 1976. Table IB, Note 7.

- [Reserved]

    - Thermo Jarrell  Ash  Corporation, 27  Forge  Parkway,  Franklin  MA  02038.

      - Method AES0029. Direct Current Plasma (DCP) Optical Emission Spec- trometric Method for Trace Elemental Analysis of Water and Wastes. 1986, Re- vised 1991. Table IB, Note 34.

      - [Reserved]

    - Thermo Scientific, 166 Cummings Center, Beverly MA 01915. Telephone: 1–800–225–1480.

      - Thermo Scientific Orion Method AQ4500, Determination of Turbidity by Nephelometry. Revision 5, March 12, 2009. Table IB, Note 67.

      - [Reserved]

    - 3M Corporation, 3M Center Build- ing 220–9E–10, St. Paul MN 55144–1000.

      - Organochlorine Pesticides and PCBs in Wastewater Using Empore TM Disk’’ Test Method 3M 0222. Revised October 28, 1994. Table IC, Note 8; Table ID, Note 8.

      - [Reserved]

    - U.S.  Geological  Survey  (USGS),

U.S. Department of the Interior, Res- ton, Virginia. Available from USGS Books and Open-File Reports (OFR) Section, Federal Center, Box 25425, Denver, CO 80225.

- OFR 76–177, Selected Methods of the  U.S.  Geological  Survey  of   Analysis of  Wastewaters.  1976.  Table  IE,  Note  2.

- OFR 91–519, Methods of Analysis by the U.S. Geological Survey National Water Quality Laboratory—Determina- tion of Organonitrogen Herbicides in Water by Solid-Phase Extraction and Capillary-Column	Gas	Chroma- tography/Mass Spectrometry With Se- lected-Ion Monitoring. 1992. Table ID, Note 14.

- OFR 92–146, Methods of Analysis by the U.S. Geological Survey National Water Quality Laboratory—Determina- tion of Total Phosphorus by a Kjeldahl Digestion Method and an Automated Colorimetric Finish That Includes Di- alysis. 1992. Table IB, Note 48.

- OFR 93–125, Methods of Analysis by the U.S. Geological Survey National Water Quality Laboratory—Determina- tion of Inorganic and Organic Constitu- ents in Water and Fluvial Sediments. 1993. Table IB, Note 51; Table IC, Note 9.

- OFR 93–449, Methods of Analysis by the U.S. Geological Survey National Water Quality Laboratory—Determina- tion of Chromium in Water by Graphite Furnace	Atomic	Absorption Spectrophotometry. 1993. Table  IB, Note 46.

- OFR 94–37, Methods of Analysis by  the  U.S.  Geological  Survey  National

#### § 136.3

Water Quality Laboratory—Determina- tion of Triazine and Other Nitrogen- containing Compounds by Gas Chroma- tography with Nitrogen Phosphorus Detectors. 1994. Table ID, Note 9.

- OFR 95–181, Methods of Analysis by the U.S. Geological Survey National Water Quality Laboratory—Determina- tion of Pesticides in Water by C-18 Solid-Phase Extraction and Capillary- Column Gas Chromatography/Mass Spectrometry With Selected-Ion Moni- toring. 1995. Table ID, Note 11.

- OFR 97–198, Methods of Anal- ysis by the U.S. Geological Survey Na- tional Water Quality Laboratory—De- termination of Molybdenum in Water by Graphite Furnace Atomic Absorp- tion Spectrophotometry. 1997. Table IB, Note 47.

- OFR 98–165, Methods of Analysis by the U.S. Geological Survey National Water Quality Laboratory—Determina- tion of Elements in Whole-Water Di- gests Using Inductively Coupled Plas- ma-Optical Emission Spectrometry and Inductively Coupled Plasma-Mass Spectrometry. 1998. Table IB, Note 50.

- OFR 98–639, Methods of Analysis by the U.S. Geological Survey National Water Quality Laboratory—Determina- tion of Arsenic and Selenium in Water and Sediment by Graphite Furnace— Atomic Absorption Spectrometry. 1999. Table IB, Note 49.

- OFR 00–170, Methods of Analysis by the U.S. Geological Survey National Water Quality Laboratory—Determina- tion of Ammonium Plus Organic Nitro- gen by  a  Kjeldahl  Digestion  Method and an Automated Photometric Finish that Includes Digest Cleanup by Gas Diffusion. 2000. Table IB, Note 45.

- Water-Resources Investigation Report 01–4098, Methods of Analysis by the U.S. Geological Survey National Water Quality Laboratory—Determina- tion of Moderate-Use Pesticides and Selected Degradates in Water by C-18 Solid-Phase Extraction and Gas Chro- matography/Mass Spectrometry. 2001. Table ID, Note 13.

- Water-Resources Investigations Report 01–4132, Methods of Analysis by the U.S. Geological Survey National Water Quality Laboratory—Determina- tion of Organic Plus Inorganic Mercury in Filtered and Unfiltered  Natural Water  With  Cold  Vapor-Atomic  Fluo-

#### 40 CFR Ch. I (7–1–17 Edition)

rescence Spectrometry. 2001. Table IB, Note 71.

- Water-Resources Investigation Report 01–4134, Methods of Analysis by the U.S. Geological Survey National Water Quality Laboratory—Determina- tion of Pesticides in Water by Graphitized Carbon-Based Solid-Phase Extraction and High-Performance Liq- uid Chormatography/Mass Spectrom- etry. 2001. Table ID, Note 12.

- Methods for Determination of In- organic Substances in Water and Flu- vial Sediments, editors, Techniques of Water-Resources  Investigations  of  the

U.S. Geological Survey, Book 5, Chap- ter A1. 1979. Table IB, Note 8.

- Methods for Determination of Inorganic Substances in  Water and Fluvial Sediments, Techniques of Water-Resources  Investigations  of  the

U.S. Geological Survey, Book 5, Chap- ter A1. 1989. Table IB, Note 2.

- Methods for the Determination of Organic Substances in Water and Fluvial Sediments. Techniques of Water-Resources  Investigations  of  the

U.S. Geological Survey, Book 5, Chap- ter A3. 1987. Table IB, Note  24;  Table ID, Note 4.

- Techniques and Methods Book 5–B1, Determination of Elements in Natural-Water,  Biota,  Sediment  and Soil Samples Using Collision/Reaction Cell Inductively Coupled Plasma-Mass Spectrometry. Chapter 1, Section B, Methods of the National Water Quality Laboratory, Book 5, Laboratory Anal- ysis. 2006. Table IB, Note 70.

- U.S. Geological Survey Tech- niques of Water-Resources Investiga- tions, Book  5,  Laboratory  Analysis, Chapter A4, Methods for Collection and Analysis of Aquatic Biological and Microbiological Samples.  1989.  Table IA, Note 4; Table IH, Note 4.

- Water Temperature—Influential Factors, Field Measurement and Data Presentation, Techniques of Water-Re- sources Investigations of the U.S. Geo- logical Survey, Book 1, Chapter D1. 1975. Table IB, Note 32.

    - Waters Corporation, 34 Maple Street, Milford MA 01757, Telephone: 508–482–2131, Fax: 508–482–3625.

- Method D6508, Test Method for De- termination    of     Dissolved    Inorganic

#### Environmental Protection Agency	§ 136.3

Anions in Aqueous Matrices Using Cap- illary Ion Electrophoresis and Chro- mate Electrolyte. Revision  2,  Decem- ber 2000. Table IB, Note 54.

- [Reserved]

- Under certain circumstances, the Regional Administrator or the Director in the Region or State where the dis- charge will occur may determine for a particular discharge that additional parameters or pollutants must be re- ported. Under such circumstances, ad- ditional test procedures for analysis of pollutants may be specified by the Re- gional Administrator, or the Director upon recommendation of the Alternate Test Procedure Program Coordinator, Washington,  DC.

- Under certain circumstances, the Administrator may approve additional alternate test procedures for nation- wide use, upon recommendation by the Alternate Test Procedure Program Co- ordinator,  Washington,  DC.

- Sample preservation procedures, container materials, and maximum al- lowable holding times for parameters are cited in Tables IA,  IB,  IC,  ID,  IE, IF, IG, and IH are prescribed in Table

II. Information in the table takes prec- edence  over  information  in  specific

methods or elsewhere. Any person may apply for a change from the prescribed preservation techniques,  container ma- terials, and maximum holding times applicable to samples taken from a spe- cific discharge. Applications for such limited use changes may be made by letters  to  the  Regional  Alternative Test Procedure (ATP) Program Coordi- nator  or  the  permitting  authority  in the Region in which the discharge will occur. Sufficient data should be pro- vided to assure such changes in sample preservation, containers or holding times do not adversely affect the integ- rity of the sample. The Regional ATP Coordinator  or  permitting  authority will review the application and then notify the applicant and the appro- priate State agency of approval or re- jection of the use of the alternate test procedure. A decision to approve or deny any request on deviations from the prescribed Table II requirements will be made within 90 days of receipt of the application by the Regional Ad- ministrator. An analyst may not  mod- ify any sample preservation and/or holding time requirements of an ap- proved method unless the requirements of this section are met.

TABLE II—REQUIRED CONTAINERS, PRESERVATION TECHNIQUES, AND HOLDING TIMES

| Parameter number/name | Container 1 | Preservation 2 3 | Maximum holding time 4 |
| --- | --- | --- | --- |
| Table IA—Bacterial Tests: 1–5. Coliform, total, fecal, and E. coli ... 6. Fecal streptococci .............................. 7. Enterococci ........................................ 8. Salmonella ......................................... Table IA—Aquatic Toxicity Tests: 9–12. Toxicity, acute and chronic .......... Table IB—Inorganic Tests: 1. Acidity ................................................ 2. Alkalinity ............................................. 4. Ammonia ............................................ 9. Biochemical oxygen demand ............. 10. Boron ............................................... 11. Bromide ............................................ Biochemical oxygen demand, car- bonaceous. Chemical oxygen demand ............... 16. Chloride ............................................ 17. Chlorine, total residual ..................... 21. Color ................................................ 23–24. Cyanide, total or available (or CATC) and free. | PA, G ............................ PA, G ............................ PA, G ............................ PA, G ............................ P, FP, G ....................... P, FP, G ....................... P, FP, G ....................... P, FP, G ....................... P, FP, G ....................... P, FP, or Quartz ........... P, FP, G ....................... P, FP G ........................ P, FP, G ....................... P, FP, G ....................... P, G .............................. P, FP, G ....................... P, FP, G ....................... | Cool, <10 C, 0.0008% Na2S2O3 5. Cool, <10 C, 0.0008% Na2S2O3 5. Cool, <10 C, 0.0008% Na2S2O3 5. Cool, <10 C, 0.0008% Na2S2O3 5. Cool, 6 C 16 ............... Cool, 6 C 18 ............... Cool, 6 C 18 ............... Cool, 6 C 18, H2SO4 to pH <2. Cool, 6 C 18 ............... HNO3 to pH <2 ............. None required ............... Cool, 6 C 18 ............... Cool, 6 C 18, H2SO4 to pH <2. None required ............... None required ............... Cool, 6 C 18 ............... Cool, 6 C 18, NaOH to pH >10 5 6, reducing agent if oxidizer present. | 8 hours. 22 23 8 hours.22 8 hours.22 8 hours.22 36 hours. 14 days. 14 days. 28 days. 48 hours. 6 months. 28 days. 48 hours. 28 days. 28 days. Analyze within 15 min- utes. 48 hours. 14 days. |

#### § 136.3

40 CFR Ch. I (7–1–17 Edition)

TABLE II—REQUIRED CONTAINERS, PRESERVATION TECHNIQUES, AND HOLDING TIMES—Continued

| Parameter number/name | Container 1 | Preservation 2 3 | Maximum holding time 4 |
| --- | --- | --- | --- |
| 25. Fluoride ............................................ 27. Hardness .......................................... 28. Hydrogen ion (pH) ........................... 31, 43. Kjeldahl and organic N .............. Table IB—Metals: 7 18. Chromium VI .................................... 35. Mercury (CVAA) ............................... 35. Mercury (CVAFS) ............................ 3, 5–8, 12, 13, 19, 20, 22, 26, 29, 30, 32–34, 36, 37, 45, 47, 51, 52, 58–60, 62, 63, 70–72, 74, 75. Metals, except boron, chromium VI, and mercury. 38. Nitrate .............................................. 39. Nitrate-nitrite .................................... 40. Nitrite ................................................ 41. Oil and grease ................................. 42. Organic Carbon ............................... 44. Orthophosphate ............................... 46. Oxygen, Dissolved Probe ................ 47. Winkler ............................................. 48. Phenols ............................................ 49. Phosphorous (elemental) ................. 50. Phosphorous, total ........................... 53. Residue, total ................................... 54. Residue, Filterable ........................... 55. Residue, Nonfilterable (TSS) ........... 56. Residue, Settleable .......................... 57. Residue, Volatile .............................. 61. Silica ................................................ 64. Specific conductance ....................... 65. Sulfate .............................................. 66. Sulfide .............................................. 67. Sulfite ............................................... 68. Surfactants ....................................... 69. Temperature .................................... 73. Turbidity ........................................... Table IC—Organic Tests: 8 13, 18–20, 22, 24–28, 34–37, 39–43, 45–47, 56, 76, 104, 105, 108–111, 113. Purgeable Halocarbons. 6, 57, 106. Purgeable aromatic hydro- carbons. 3, 4. Acrolein and acrylonitrile ............... 23, 30, 44, 49, 53, 77, 80, 81, 98, 100, 112. Phenols 11. 7, 38. Benzidines 11 12 ............................ 14, 17, 48, 50–52. Phthalate esters 11 .. | P ................................... P, FP, G ....................... P, FP, G ....................... P, FP, G ....................... P, FP, G ....................... P, FP, G ....................... FP, G; and FP-lined cap 17. P, FP, G ....................... P, FP, G ....................... P, FP, G ....................... P, FP, G ....................... G ................................... P, FP, G ....................... P, FP, G ....................... G, Bottle and top .......... G, Bottle and top .......... G ................................... G ................................... P, FP, G ....................... P, FP, G ....................... P, FP, G ....................... P, FP, G ....................... P, FP, G ....................... P, FP, G ....................... P or Quartz ................... P, FP, G ....................... P, FP, G ....................... P, FP, G ....................... P, FP, G ....................... P, FP, G ....................... P, FP, G ....................... P, FP, G ....................... G, FP-lined septum ...... G, FP-lined septum ...... G, FP-lined septum ...... G, FP-lined cap ............ G, FP-lined cap ............ G, FP-lined cap ............ | None required ............... HNO3 or H2SO4 to pH <2. None required ............... Cool, 6 C 18, H2SO4 to pH <2. Cool, 6 C 18, pH = 9.3–9.7 20. HNO3 to pH <2 ............. 5 mL/L 12N HCl or 5 mL/L BrCl 17. HNO3 to pH <2, or at least 24 hours prior to analysis 19. Cool, 6 C 18 ............... Cool, 6 C 18, H2SO4 to pH <2. Cool, 6 C 18 ............... Cool to 6 C 18, HCl or H2SO4 to pH <2. Cool to 6 C 18, HCl, H2SO4, or H3PO4 to pH <2. Cool, to 6 C 18 24 ....... None required ............... Fix on site and store in dark. Cool, 6 C 18, H2SO4 to pH <2. Cool, 6 C 18 ............... Cool, 6 C 18, H2SO4 to pH <2. Cool, 6 C 18 ............... Cool, 6 C 18 ............... Cool, 6 C 18 ............... Cool, 6 C 18 ............... Cool, 6 C 18 ............... Cool, 6 C 18 ............... Cool, 6 C 18 ............... Cool, 6 C 18 ............... Cool, 6 C 18, add zinc acetate plus sodium hydroxide to pH >9. None required ............... Cool, 6 C 18 ............... None required ............... Cool, 6 C 18 ............... Cool, 6 C 18, 0.008% Na2S2O 5. 3 Cool, 6 C 18, 0.008% Na2S2O3 5, HCl to pH 2 9. Cool, 6 C 18, 0.008% Na2S2O3, pH to 4–510. Cool, 6 C 18, 0.008% Na2S2O3. Cool, 6 C 18, 0.008% Na2S2O 5. 3 Cool, 6 C 18 ............... | 28 days. 6 months. Analyze within 15 min- utes. 28 days. 28 days. 28 days. 90 days.17 6 months. 48 hours. 28 days. 48 hours. 28 days. 28 days. Filter within 15 minutes; Analyze within 48 hours. Analyze within 15 min- utes. 8 hours. 28 days. 48 hours. 28 days. 7 days. 7 days. 7 days. 48 hours. 7 days. 28 days. 28 days. 28 days. 7 days. Analyze within 15 min- utes. 48 hours. Analyze. 48 hours. 14 days. 14 days.9 14 days.10 7 days until extraction, 40 days after extrac- tion. 7 days until extrac- tion.13 7 days until extraction, 40 days after extrac- tion. |

#### Environmental Protection Agency	§ 136.3

TABLE II—REQUIRED CONTAINERS, PRESERVATION TECHNIQUES, AND HOLDING TIMES—Continued

| Parameter number/name | Container 1 | Preservation 2 3 | Maximum holding time 4 |
| --- | --- | --- | --- |
| 82–84. Nitrosamines 11 14 ...................... 88–94. PCBs 11 ...................................... 54, 55, 75, 79. Nitroaromatics and isophorone 11. 1, 2, 5, 8–12, 32, 33, 58, 59, 74, 78, 99, 101. Polynuclear aromatic hydro- carbons 11. 15, 16, 21, 31, 87. Haloethers 11 ........... 29, 35–37, 63–65, 107. Chlorinated hy- drocarbons 11. 60–62, 66–72, 85, 86, 95–97, 102, 103. CDDs/CDFs 11. Aqueous Samples: Field and Lab Pres- ervation. Solids and Mixed-Phase Samples: Field Preservation. Tissue Samples: Field Preservation ...... Solids, Mixed-Phase, and Tissue Sam- ples: Lab Preservation. 114–118. Alkylated phenols ................... Adsorbable Organic Halides (AOX) Chlorinated Phenolics .................... Table ID—Pesticides Tests: 1–70. Pesticides 11 ................................. Table IE—Radiological Tests: 1–5. Alpha, beta, and radium ................ Table IH—Bacterial Tests: 1. E. coli ................................................. 2. Enterococci ........................................ Table IH—Protozoan Tests: 8. Cryptosporidium ................................. 9. Giardia ............................................... | G, FP-lined cap ............ G, FP-lined cap ............ G, FP-lined cap ............ G, FP-lined cap ............ G, FP-lined cap ............ G, FP-lined cap ............ G ................................... G ................................... G ................................... G ................................... G ................................... G ................................... ....................................... G, FP-lined cap ............ P, FP, G ....................... PA, G ............................ PA, G ............................ LDPE; field filtration ...... LDPE; field filtration ...... | Cool, 6 C18, store in dark, 0.008% Na2S2O 5. 3 Cool, 6 C 18 ............... Cool, 6 C 18, store in dark, 0.008% Na2S2O 5. 3 Cool, 6 C 18, store in dark, 0.008% Na2S2O 5. 3 Cool, 6 C 18, 0.008% Na2S2O 5. 3 Cool, 6 C 18 ............... Cool, 6 C 18, 0.008% Na2S2O 5, pH <9. 3 Cool, 6 C 18 ............... Cool, 6 C 18 ............... Freeze, ¥10 C ......... Cool, <6 C, H2SO4 to pH <2. Cool, <6 C, 0.008% Na2S2O3 HNO3 to pH <2. Cool, <6 C, 0.008% Na2S2O3 H2SO4 to pH <2. Cool, 6 C 18, pH 5–9– 15. HNO3 to pH <2 ............. Cool, <10 C, 0.0008% Na2S2O 5. 3 Cool, <10 C, 0.0008% Na2S2O3 5. 1–10 C ........................ 1–10 C ........................ | 7 days until extraction, 40 days after extrac- tion. 1 year until extraction, 1 year after extraction. 7 days until extraction, 40 days after extrac- tion. 7 days until extraction, 40 days after extrac- tion. 7 days until extraction, 40 days after extrac- tion. 7 days until extraction, 40 days after extrac- tion. 1 year. 7 days. 24 hours. 1 year. 28 days until extraction, 40 days after extrac- tion. Hold at least 3 days, but not more than 6 months. 30 days until acetylation, 30 days after acetylation. 7 days until extraction, 40 days after extrac- tion. 6 months. 8 hours.22 8 hours.22 96 hours.21 96 hours.21 |

1 ‘‘P’’ is for polyethylene; ‘‘FP’’ is fluoropolymer (polytetrafluoroethylene (PTFE); Teflon), or other fluoropolymer, unless stated otherwise  in  this  Table  II;  ‘‘G’’  is  glass;  ‘‘PA’’  is  any  plastic  that  is  made  of  a  sterilizable  material  (polypropylene  or other autoclavable plastic); ‘‘LDPE’’ is low density polyethylene.

2 Except where noted in this Table II and the method for the parameter, preserve each grab sample within 15 minutes of col- lection. For a composite sample collected with an automated sample (e.g., using a 24-hour composite sample; see 40 CFR 122.21(g)(7)(i) or 40 CFR Part 403, Appendix E), refrigerate the sample at 6 C during collection unless specified otherwise in this Table II or in the method(s). For a composite sample to be split into separate aliquots for preservation and/or analysis, main- tain the sample at 6 C, unless specified otherwise in this Table II or in the method(s), until collection, splitting, and preservation is completed. Add the preservative to the sample container prior to sample collection when the preservative will not compromise the integrity of a grab sample, a composite sample, or aliquot split from a composite sample within 15 minutes of collection. If a composite measurement is required but a composite sample would compromise sample integrity, individual grab samples must be collected at prescribed time intervals (e.g., 4 samples over the course of a day, at 6-hour intervals). Grab samples must be analyzed separately and the concentrations averaged. Alternatively, grab samples may be collected in the field and composited in the laboratory if the compositing procedure produces results equivalent to results produced by arithmetic averaging of results of analysis of individual grab samples. For examples of laboratory compositing procedures, see EPA Method 1664 Rev. A (oil and grease) and the procedures at 40 CFR 141.34(f)(14)(iv) and (v) (volatile organics).

3 When any sample is to be shipped by common carrier or sent via the U.S. Postal Service, it must comply with the Depart- ment of Transportation Hazardous Materials Regulations (49 CFR part 172). The person offering such material for transportation is responsible for ensuring such compliance. For the preservation requirement of Table II, the Office of Hazardous Materials, Ma- terials Transportation Bureau, Department of Transportation has determined that the Hazardous Materials Regulations do not apply to the following materials: Hydrochloric acid (HCl) in water solutions at concentrations of 0.04% by weight or less (pH about 1.96 or greater; Nitric acid (HNO3) in water solutions at concentrations of 0.15% by weight or less (pH about 1.62 or great- er); Sulfuric acid (H2SO4) in water solutions at concentrations of 0.35% by weight or less (pH about 1.15 or greater); and Sodium hydroxide (NaOH) in water solutions at concentrations of 0.080% by weight or less (pH about 12.30 or less).

#### § 136.3

40 CFR Ch. I (7–1–17 Edition)

4 Samples should be analyzed as soon as possible after collection. The times listed are the maximum times that samples may be held before the start of analysis and still be considered valid. Samples may be held for longer periods only if the permittee or monitoring laboratory has data on file to show that, for the specific types of samples under study, the analytes are stable for the longer time, and has received a variance from the Regional Administrator under Sec. 136.3(e). For a grab sample, the holding time begins at the time of collection. For a composite sample collected with an automated sampler (e.g., using a 24-hour com- posite sampler; see 40 CFR 122.21(g)(7)(i) or 40 CFR part 403, Appendix E), the holding time begins at the time of the end of collection of the composite sample. For a set of grab samples composited in the field or laboratory, the holding time begins at the time of collection of the last grab sample in the set. Some samples may not be stable for the maximum time period given in the table. A permittee or monitoring laboratory is obligated to hold the sample for a shorter time if it knows that a shorter time is necessary to maintain sample stability. See 136.3(e) for details. The date and time of collection of an individual grab sample is the date and time at which the sample is collected. For a set of grab samples to be composited, and that are all collected on the same calendar date, the date of collection is the date on which the samples are collected. For a set of grab samples to be com- posited, and that are collected across two calendar dates, the date of collection is the dates of the two days; e.g., November 14–

  - For a composite sample collected automatically on a given date, the date of collection is the date on which the sample is col- lected. For a composite sample collected automatically, and that is collected across two calendar dates, the date of collection is the dates of the two days; e.g., November 14–15. For static-renewal toxicity tests, each grab or composite sample may also be used to prepare test solutions for renewal at 24 h, 48 h, and/or 72 h after first use, if stored at 0–6 C, with minimum head space.

5 ASTM D7365–09a specifies treatment options for samples containing oxidants (e.g., chlorine). Also, Section 9060A of Stand- ard Methods for the Examination of Water and Wastewater (20th and 21st editions) addresses dechlorination procedures.

6 Sampling, preservation and mitigating interferences in water samples for analysis of cyanide are described in ASTM D7365– 09a. There may be interferences that are not mitigated by the analytical test methods or D7365–09a. Any technique for removal or suppression of interference may be employed, provided the laboratory demonstrates that it more accurately measures cyanide through quality control measures described in the analytical test method. Any removal or suppression technique not described in D7365–09a or the analytical test method must be documented along with supporting data.

7 For dissolved metals, filter grab samples within 15 minutes of collection and before adding preservatives. For a composite sample collected with an automated sampler (e.g., using a 24-hour composite sampler; see 40 CFR 122.21(g)(7)(i) or 40 CFR Part 403, Appendix E), filter the sample within 15 minutes after completion of collection and before adding preservatives. If it is known or suspected that dissolved sample integrity will be compromised during collection of a composite sample collected auto- matically over time (e.g., by interchange of a metal between dissolved and suspended forms), collect and filter grab samples to be composited (footnote 2) in place of a composite sample collected automatically.

8 Guidance applies to samples to be analyzed by GC, LC, or GC/MS for specific compounds.

9 If the sample is not adjusted to pH 2, then the sample must be analyzed within seven days of sampling.

10 The pH adjustment is not required if acrolein will not be measured. Samples for acrolein receiving no pH adjustment must be analyzed within 3 days of sampling.

11 When the extractable analytes of concern fall within a single chemical category, the specified preservative and maximum holding times should be observed for optimum safeguard of sample integrity (i.e., use all necessary preservatives and hold for the shortest time listed). When the analytes of concern fall within two or more chemical categories, the sample may be preserved by cooling to 6 C, reducing residual chlorine with 0.008% sodium thiosulfate, storing in the dark, and adjusting the pH to 6–9; samples preserved in this manner may be held for seven days before extraction and for forty days after extraction. Exceptions to this optional preservation and holding time procedure are noted in footnote 5 (regarding the requirement for thiosulfate reduc- tion), and footnotes 12, 13 (regarding the analysis of benzidine).

12 If 1,2-diphenylhydrazine is likely to be present, adjust the pH of the sample to 4.0 0.2 to prevent rearrangement to benzi- dine.

13 Extracts may be stored up to 30 days at <0 C.

14 For the analysis of diphenylnitrosamine, add 0.008% Na2S2O3 and adjust pH to 7–10 with NaOH within 24 hours of sam- pling.

15 The pH adjustment may be performed upon receipt at the laboratory and may be omitted if the samples are extracted within 72 hours of collection. For the analysis of aldrin, add 0.008% Na2S2O3.

16 Place sufficient ice with the samples in the shipping container to ensure that ice is still present when the samples arrive at the laboratory. However, even if ice is present when the samples arrive, immediately measure the temperature of the samples and confirm that the preservation temperature maximum has not been exceeded. In the isolated cases where it can be docu- mented that this holding temperature cannot be met, the permittee can be given the option of on-site testing or can request a variance. The request for a variance should include supportive data which show that the toxicity of the effluent samples is not re- duced because of the increased holding temperature. Aqueous samples must not be frozen. Hand-delivered samples used on the day of collection do not need to be cooled to 0 to 6 C prior to test initiation.

17 Samples collected for the determination of trace level mercury (<100 ng/L) using EPA Method 1631 must be collected in tightly-capped fluoropolymer or glass bottles and preserved with BrCl or HCl solution within 48 hours of sample collection. The time to preservation may be extended to 28 days if a sample is oxidized in the sample bottle. A sample collected for dissolved trace level mercury should be filtered in the laboratory within 24 hours of the time of collection. However, if circumstances pre- clude overnight shipment, the sample should be filtered in a designated clean area in the field in accordance with procedures given in Method 1669. If sample integrity will not be maintained by shipment to and filtration in the laboratory, the sample must be filtered in a designated clean area in the field within the time period necessary to maintain sample integrity. A sample that has been collected for determination of total or dissolved trace level mercury must be analyzed within 90 days of sample collection.

18 Aqueous samples must be preserved at 6 C, and should not be frozen unless data demonstrating that sample freezing does not adversely impact sample integrity is maintained on file and accepted as valid by the regulatory authority. Also, for pur- poses of NPDES monitoring, the specification of ‘‘C’’ is used in place of the ‘‘4 C’’ and ‘‘<4 C’’ sample temperature require- ments listed in some methods. It is not necessary to measure the sample temperature to three significant figures (1/100th of 1 degree); rather, three significant figures are specified so that rounding down to 6 C may not be used to meet the 6 C require- ment. The preservation temperature does not apply to samples that are analyzed immediately (less than 15 minutes).

19 An aqueous sample may be collected and shipped without acid preservation. However, acid must be added at least 24 hours before analysis to dissolve any metals that adsorb to the container walls. If the sample must be analyzed within 24 hours of collection, add the acid immediately (see footnote 2). Soil and sediment samples do not need to be preserved with acid. The allowances in this footnote supersede the preservation and holding time requirements in the approved metals methods.

20 To achieve the 28-day holding time, use the ammonium sulfate buffer solution specified in EPA Method 218.6. The allow- ance in this footnote supersedes preservation and holding time requirements in the approved hexavalent chromium methods, un- less this supersession would compromise the measurement, in which case requirements in the method must be followed.

21 Holding time is calculated from time of sample collection to elution for samples shipped to the laboratory in bulk and cal- culated from the time of sample filtration to elution for samples filtered in the field.

22 Sample analysis should begin as soon as possible after receipt; sample incubation must be started no later than 8 hours from time of collection.

23 For fecal coliform samples for sewage sludge (biosolids) only, the holding time is extended to 24 hours for the following sample types using either EPA Method 1680 (LTB–EC) or 1681 (A–1): Class A composted, Class B aerobically digested, and Class B anaerobically digested.

24 The immediate filtration requirement in orthophosphate measurement is to assess the dissolved or bio-available form of orthophosphorus (i.e., that which passes through a 0.45-micron filter), hence the requirement to filter the sample immediately upon collection (i.e., within 15 minutes of collection).

#### Environmental Protection Agency	§ 136.4

[38 FR 28758, Oct. 16, 1973]

EDITORIAL NOTE: For FEDERAL REGISTER citations affecting § 136.3, see the List of CFR Sec- tions Affected, which appears in the Finding Aids section of the printed volume

##### § 136.4 Application for and approval of alternate test procedures for na- tionwide use.

    - A  written  application  for   review of an alternate test  procedure  (alter- nate method) for nationwide use  may be made by letter via email or by hard copy in triplicate to the National Al- ternate Test Procedure (ATP) Program Coordinator  (National  Coordinator), Office of Science and Technology (4303T), Office of Water, U.S. Environ- mental Protection Agency, 1200 Penn- sylvania Ave. NW., Washington, DC 20460. Any application for an alternate test procedure (ATP) under this para- graph  (a)  shall:

      - Provide the name and address of the responsible person or firm making the  application.

      - Identify the pollutant(s) or pa- rameter(s) for which nationwide ap- proval of an alternate test procedure is being requested.

      - Provide a detailed description of the proposed alternate test procedure, together with references to published or other studies confirming the general applicability of the alternate test pro- cedure for the analysis of the pollut- ant(s) or parameter(s) in wastewater discharges from representative and specified industrial or other categories.

      - Provide comparability data for the performance of the proposed alter- native test procedure compared to the performance of the reference method.

    - The National Coordinator may re- quest additional information and anal- yses from the applicant in order to de- termine whether the alternate test pro- cedure satisfies the applicable require- ments of this part.

    - Approval for nationwide use. (1) After a review of the application and any additional analyses requested from the applicant, the National Coordi- nator will notify the applicant, in writ- ing, of acceptance or rejection of the alternate test procedure for nationwide use in CWA programs. If the applica- tion is not approved, the National Co- ordinator will specify what additional

information might lead to a reconsid- eration of the application, and notify the Regional Alternate Test Procedure Coordinators of such rejection. Based on the National Coordinator’s rejection of a proposed alternate test procedure and an assessment of any approvals for limited uses for the unapproved meth- od, the Regional ATP Coordinator or permitting authority may decide to withdraw approval of the method for limited use in the Region.

- Where the  National  Coordinator approved an applicant’s request for na- tionwide use of an alternate test proce- dure, the National Coordinator will no- tify the applicant that the National Coordinator will recommend rule- making to approve the alternate test procedure. The National Coordinator will notify the Regional ATP Coordi- nator or permitting authorities that they may consider approval of this al- ternate test procedure for limited use in their Regions based on the informa- tion and data provided in the appli- cant’s application. The Regional ATP Coordinator or permitting authority will grant approval on a case-by-case basis prior to use of the alternate test procedure for compliance analyses until the alternate test procedure is approved by publication in a final rule in  the  FEDERAL  REGISTER.

- EPA will propose to amend 40 CFR part 136 to include the alternate test procedure in § 136.3. EPA shall make available  for  review  all  the  factual bases for its proposal, including any performance data submitted by the ap- plicant and any available  EPA  analysis of  those  data.

- Following public comment, EPA shall  publish  in  the  FEDERAL  REGISTER a final decision on whether to amend 40 CFR part 136 to include the alternate test procedure as an approved analyt- ical  method.

- Whenever the National Coordi- nator has approved an applicant’s re- quest for nationwide use of an alter- nate test procedure, any person may request an approval of the method for

#### § 136.5

limited  use  under  § 136.5  from  the  EPA Region.

[77 FR 29809, May 18, 2012]

##### § 136.5   Approval of alternate test pro- cedures for limited use.

  - Any person may request the Re- gional Alternate Test Procedure (ATP) Coordinator or permitting authority to approve the use of an alternate test procedure in the Region.

  - When the request for the use of an alternate test procedure concerns  use in a State with an NPDES permit pro- gram approved pursuant to section 402 of the Act, the requestor shall first submit an application for  limited  use to the Director of the State agency having responsibility for issuance of NPDES permits within such State (i.e., permitting  authority).  The  Director will forward the application to the Re- gional ATP Coordinator or permitting authority with a recommendation  for or against approval.

  - Any application for approval of an alternate test procedure for limited use may be made by letter, email or by hard copy. The application shall in- clude the following:

    - Provide the name and address of the applicant and the applicable ID number of the existing or pending per- mit and issuing agency for which use of the alternate test procedure is re- quested, and the discharge serial num- ber.

    - Identify the pollutant or param- eter for which approval of an alternate test procedure is being requested.

    - Provide justification for using testing procedures other than those specified  in  Tables  IA  through  IH  of

§ 136.3, or in the NPDES permit.

    - Provide a detailed description of the proposed alternate test procedure, together with references to published studies of the applicability of the alter- nate test procedure to the effluents in question.

    - Provide comparability data for the performance of the proposed alter- nate test procedure compared to the performance of the reference method.

  - Approval for limited use. (1) After a review of the application by the Alter- nate Test Procedure Regional ATP Co- ordinator or permitting authority, the Regional  ATP  Coordinator  or  permit-

#### 40 CFR Ch. I (7–1–17 Edition)

ting authority notifies  the  applicant and the appropriate State agency of ap- proval or rejection of the use of the al- ternate test procedure. The  approval may be restricted to use only with re- spect to a specific discharge or facility (and its laboratory) or, at the discre- tion of the Regional  ATP  Coordinator or permitting authority, to all dis- charger or facilities (and their associ- ated laboratories) specified in the ap- proval for the Region. If the applica- tion is not approved, the Regional ATP Coordinator or permitting  authority shall specify what additional informa- tion might lead to a reconsideration of the  application.

- The Regional ATP Coordinator or permitting authority will forward a copy of every approval and rejection notification to the National Alternate Test Procedure Coordinator.

[77 FR 29809, May 18, 2012]

##### § 136.6   Method modifications and ana- lytical requirements.

  - Definitions of terms used in this sec- tion—(1) Analyst means the person or laboratory using a test procedure (ana- lytical method) in this part.

- Chemistry of the method means the reagents and reactions used in a test procedure that allow determination of the analyte(s) of interest in an environ- mental sample.

- Determinative technique means the way in which an analyte is identified and quantified (e.g., colorimetry, mass spectrometry).

- Equivalent performance means that the modified method produces results that meet or exceed the QC acceptance criteria of the approved method.

- Method-defined analyte means an analyte defined solely by the method used to determine the analyte. Such an analyte may be a physical parameter, a parameter that is not a specific chem- ical, or a parameter that may be com- prised of a number of substances. Ex- amples of such analytes include tem- perature, oil and grease, total sus- pended solids, total phenolics,  tur- bidity, chemical oxygen demand, and biochemical oxygen demand.

- QC means ‘‘quality control.’’

  - Method modifications. (1) If the un- derlying   chemistry   and   determinative

#### Environmental Protection Agency	§ 136.6

technique in a modified method are es- sentially the same as an approved part

136 method, then the modified method is an equivalent and acceptable alter- native to the approved method pro- vided the requirements of this section are met. However, those who develop or use a modification to an approved (part

136) method must document that the performance of the modified method, in the matrix to which the  modified method will be applied, is equivalent to the performance of the approved meth- od. If such a demonstration cannot be made and documented, then the modi- fied method is not an acceptable alter- native to the approved method. Sup- porting documentation must, if appli- cable, include the routine initial dem- onstration of  capability  and  ongoing QC including determination of  preci- sion and accuracy,  detection  limits, and matrix spike  recoveries.  Initial demonstration of capability typically includes analysis of four replicates of a mid-level standard and a method detec- tion limit study. Ongoing quality con- trol typically includes method blanks, mid-level laboratory control samples, and matrix spikes (QC is as specified in the method). The method is considered equivalent if the quality control re- quirements in the reference method are achieved. The method user’s Standard Operating Procedure (SOP) must clear- ly document the modifications made to the reference method. Examples of al- lowed method modifications are  listed in this section. The user must notify their permitting authority  of  the  in- tent to use a modified method. Such notification should be of the form ‘‘Method xxx has been modified within the flexibility allowed in 40 CFR 136.6.’’ The user may indicate the specific paragraph of § 136.6 allowing the meth- od modification. However, specific de- tails of the modification need not be provided, but must be documented in the Standard Operating  Procedure (SOP). If the method user is uncertain whether a method modification is al- lowed, the Regional ATP  Coordinator or permitting authority should be con- tacted for approval prior to imple- menting the modification. The method user should also complete necessary performance checks to verify that ac- ceptable  performance  is  achieved  with

the method modification prior to anal- yses of compliance samples.

- Requirements. The modified meth- od must be sufficiently sensitive and meet or exceed performance of the ap- proved method(s) for the analyte(s) of interest, as documented by meeting the initial and ongoing quality control re- quirements in the method.

  - Requirements for establishing equiv- alent performance. If the approved method contains QC tests and QC ac- ceptance criteria,  the modified  method must use these QC tests and the modi- fied method must meet the QC accept- ance criteria with the following condi- tions:

    - The analyst may only rely on QC tests and QC acceptance criteria in a method if it includes wastewater ma- trix QC tests and QC acceptance cri- teria (e.g., matrix spikes) and both ini- tial (start-up) and ongoing QC tests and QC acceptance criteria.

    - If the approved method does not contain QC tests and QC acceptance criteria or if the QC tests and QC ac- ceptance criteria in the method do not meet the requirements of this section, then the analyst must employ QC tests published in the ‘‘equivalent’’ of a Part 136 method that has such QC, or the es- sential QC requirements specified at 136.7, as applicable. If the approved method is from a compendium or VCSB and the QA/QC requirements are pub- lished in other parts of that organiza- tion’s compendium rather than within the Part 136 method then that part of the organization’s compendium must be used for the QC tests.

    - In addition, the analyst must per- form ongoing QC tests, including as- sessment of performance of the modi- fied method on the sample matrix (e.g., analysis of a matrix spike/matrix spike duplicate pair for every twenty sam- ples), and analysis of an ongoing preci- sion and recovery sample (e.g., labora- tory fortified blank or blank spike) and a blank with each batch of 20 or fewer samples.

    - If the performance of the modi- fied method in the wastewater matrix or reagent water does not meet or ex- ceed the QC acceptance criteria, the method modification may not be used.

#### § 136.6

  - Requirements for documentation. The modified method must be docu- mented in a method write-up or an ad- dendum that describes the modifica- tion(s) to the approved method prior to the use of the method for compliance purposes. The write-up or addendum must include a reference number (e.g., method number), revision number, and revision date so that it may be ref- erenced accurately. In addition, the or- ganization that uses the modified method must document the results of QC tests and keep these records, along with a copy of the method write-up or addendum, for review by an auditor.

- Restrictions. An analyst may not modify an approved Clean Water Act analytical method for a method-de- fined analyte. In addition, an analyst may not modify an approved method if the modification would result in meas- urement of a different form or species of an analyte. Changes in method pro- cedures are not allowed if such changes would alter the defined chemistry (i.e., method principle) of the unmodified method.  For  example,  phenol  method

420.1 or 420.4 defines phenolics as ferric iron  oxidized  compounds  that  react with 4-aminoantipyrine (4-AAP) at pH 10 after being distilled from acid solu- tion. Because  total  phenolics  rep- resents a group of compounds that all react at different efficiencies  with  4- AAP, changing test conditions  likely would change the behavior of these dif- ferent phenolic compounds. An analyst may not modify any sample collection, preservation, or holding time require- ments of an approved method. Such modifications to sample collection, preservation, and holding time require- ments do not fall within the  scope  of the flexibility allowed at § 136.6.  Meth- od flexibility refers to modifications of the analytical procedures used for identification and measurement of the analyte only and does not apply to sample collection, preservation,  or holding time procedures, which  may only     be     modified     as     specified     in

§ 136.3(e).

- Allowable changes. Except as noted under paragraph (b)(3) of this section, an analyst  may  modify  an  approved test procedure (analytical method) pro- vided that the  underlying  reactions and  principles  used  in  the  approved

#### 40 CFR Ch. I (7–1–17 Edition)

method remain essentially  the  same, and provided that the requirements of this section are met. If equal or better performance can be obtained with an alternative reagent, then  it  is  allowed. A laboratory wishing to use these modifications must demonstrate ac- ceptable method performance by per- forming and documenting all applica- ble initial demonstration of capability and ongoing QC tests and meeting all applicable QC acceptance criteria as described in § 136.7. Some examples of the allowed types of changes, provided the requirements of  this  section  are met include:

- Changes between manual method, flow analyzer, and discrete instrumen- tation.

- Changes in chromatographic col- umns or temperature programs.

- Changes between automated and manual sample preparation, such as di- gestions, distillations, and extractions; in-line sample preparation is an ac- ceptable form of automated sample preparation for CWA methods.

- In general, ICP–MS is a sensitive and selective detector for metal anal- ysis; however isobaric interference can cause problems for quantitative deter- mination, as well as identification based on the isotope pattern. Inter- ference reduction technologies, such as collision cells or reaction cells, are de- signed to reduce the effect of spectroscopic interferences that may bias results for the element of interest. The use of interference reduction tech- nologies is allowed, provided the meth- od performance specifications relevant to ICP–MS measurements are met.

- The use of EPA  Method 200.2 or the sample preparation steps from EPA Method 1638, including the use of closed-vessel digestion, is allowed for EPA Method 200.8, provided the method performance specifications relevant to the ICP–MS are met.

- Changes in pH adjustment re- agents. Changes in compounds used to adjust pH are acceptable as long as they do not produce interference. For example, using a different acid to ad- just pH in colorimetric methods.

- Changes in buffer reagents are acceptable provided that the changes do not produce interferences.

#### Environmental Protection Agency	§ 136.6

- Changes in the order of reagent addition are acceptable provided that the change does not alter the chem- istry and does not produce an inter- ference. For example, using the same reagents, but adding them in different order, or preparing them in combined or separate solutions (so they can be added separately), is allowed, provided reagent stability or method perform- ance is equivalent or improved.

- Changes in calibration range (provided that the modified range cov- ers any relevant regulatory limit and the method performance specifications for calibration are met).

- Changes in calibration model. (A) Linear calibration models do not ade- quately fit calibration data with one or two inflection points. For example, vendor-supplied data acquisition and processing software on some instru- ments may provide quadratic fitting functions to handle such situations. If

the calibration data for a particular analytical method routinely display quadratic character, using quadratic fitting functions may be acceptable. In such cases, the minimum number of calibrators for second order fits should be six, and in no case should concentra- tions be extrapolated for instrument responses that exceed that of the most concentrated calibrator. Examples of methods with nonlinear calibration functions include chloride by SM4500– Cl–E–1997, hardness by EPA Method 130.1, cyanide by ASTM D6888 or OIA1677, Kjeldahl nitrogen by PAI– DK03, and anions by EPA Method 300.0.

- As an alternative to using the av- erage response factor, the quality of the calibration may be evaluated using the Relative Standard Error  (RSE). The acceptance criterion for the RSE is the same as the acceptance criterion for Relative Standard Deviation (RSD), in the method. RSE is calculated as:

Where:

xi = Calculated concentration at level i

xi  = Actual concentration of the calibration level i

n = Number of calibration points

p = Number of terms in the fitting equation (average = 1, linear = 2, quadratic = 3)

- Using the RSE as a metric has the added advantage of allowing the same numerical standard to be applied to the calibration model, regardless of the form of the model. Thus, if a meth- od states that the RSD should be 20% for the traditional linear  model through the origin, then the RSE ac- ceptance limit can remain 20% as well. Similarly, if a method  provides an RSD acceptance limit of 15%, then that same figure can be used as the ac- ceptance limit for the RSE. The RSE may be used as an alternative to cor- relation coefficients and coefficients of determination  for  evaluating  calibra-

tion curves for any of the methods at part 136. If the method includes a nu- merical criterion for the RSD, then the same numerical value is used for the RSE. Some older methods do not in- clude any criterion for the calibration curve—for these methods, if  RSE  is used the value should be 20%. Note that the use of the  RSE  is  included  as an alternative to the use of the correla- tion coefficient  as  a  measure  of  the suitability of a calibration curve. It  is not necessary to  evaluate  both  the RSE  and  the  correlation  coefficient.

- Changes in equipment such as equipment from a vendor different from the one specified in the method.

- The use of micro or midi dis- tillation apparatus in place of macro distillation apparatus.

- The use of prepackaged re- agents.

#### § 136.6

- The use of digital titrators and methods where the underlying chem- istry used for the determination is similar to that used in the approved method.

- Use of selected ion monitoring (SIM) mode for analytes that cannot be effectively analyzed in  full-scan  mode and  reach   the   required   sensitivity. False positives are more of a concern when using SIM analysis, so at a min- imum, one quantitation and two quali- fying ions must be monitored for each analyte (unless fewer than  three  ions with intensity greater than 15% of the base peak are available). The ratio of each of the two qualifying ions to the quantitation ion must be evaluated and should agree with the ratio  observed  in an authentic standard within 20 per- cent. Analyst judgment must be  ap- plied to the evaluation of ion ratios be- cause the ratios can be affected by co- eluting compounds present in the sam- ple matrix. The signal-to-noise ratio of the least sensitive  ion  should  be  at least 3:1. Retention time in the sample should match within 0.05 minute of an authentic standard analyzed under identical conditions. Matrix inter- ferences can cause minor shifts in re- tention time and may be  evident  as shifts in the retention times of the in- ternal standards. The total scan time should be such that  a  minimum  of eight scans are obtained per chromatographic    peak.

- Changes are allowed in purge- and-trap sample volumes or operating conditions. Some examples are:

- Changes in purge time and purge- gas flow rate. A change in purge  time and purge-gas flow rate is allowed pro- vided that sufficient total purge vol- ume is used to achieve the required minimum detectible concentration and calibration range for all compounds. In general, a  purge rate in  the range 20– 200 mL/min and a total purge volume in the range 240–880 mL are recommended.

- Use of nitrogen or helium as a purge gas, provided that the required sensitivities for all compounds are met.

- Sample temperature during the purge state. Gentle heating of the sam- ple during purging (e.g., 40 C) in- creases purging efficiency of hydro- philic   compounds   and   may   improve

#### 40 CFR Ch. I (7–1–17 Edition)

sample-to-sample repeatability because all samples are purged under precisely the same conditions.

- Trap sorbent. Any trap design is acceptable, provided that the data ac- quired meet all QC criteria.

- Changes to the  desorb time. Shortening the desorb time (e.g., from4 minutes to 1 minute) may not affect compound recoveries, and can shorten overall cycle time and significantly re- duce the amount of  water  introduced to the analytical system, thus improv- ing the precision of analysis, especially for water-soluble analytes. A desorb time of four minutes is recommended, however a shorter desorb time may be used, provided that all QC  specifica- tions in the method are met.

- Use of water management tech- niques is allowed. Water is always col- lected on the trap along with the analytes and is a significant inter- ference for analytical systems (GC and GC/MS). Modern water management techniques (e.g., dry purge or condensa- tion points) can remove moisture from the sample stream and improve analyt- ical  performance.

- The following modifications are allowable when performing EPA Method 625: The base/neutral and acid fractions may be added together and analyzed as one extract, provided that the analytes can be reliably identified and quantified in the combined ex- tracts; the pH extraction sequence may be reversed to better separate acid and neutral components; neutral compo- nents may be extracted with either acid or base components; a smaller sample volume may be used to mini- mize matrix interferences provided ma- trix interferences are demonstrated and documented; alternative surrogate and internal standard concentrations other than those specified in the meth- od are acceptable, provided that meth- od performance is not degraded; an al- ternative concentration range may be used for the calibration other than the range specified in the method; the sol- vent for the calibration standards may be changed to match the solvent of the final sample extract.

#### Environmental Protection Agency	§ 136.7

- If the characteristics of a wastewater matrix prevent efficient re- covery of organic pollutants and pre- vent the method from meeting QC re- quirements, the analyst may  attempt to resolve the issue by adding salts to the sample, provided that such salts do not react with or introduce the target pollutant into the sample (as evidenced by the analysis of method blanks, lab- oratory control samples, and spiked samples that also contain such salts), and that all requirements of paragraph (b)(2) of this section are met. Samples having residual chlorine or other halo- gen must be dechlorinated prior to the addition of such salts.

- If the characteristics of a waste- water matrix result in poor sample dis- persion or reagent deposition on equip- ment and prevent the analyst from meeting QC requirements, the analyst may attempt to resolve the issue by adding a inert surfactant that does not affect the chemistry of the method, such as Brij-35 or sodium dodecyl sul- fate (SDS), provided that such surfac- tant does not react with or introduce the target pollutant into the sample (as evidenced by the analysis of method blanks, laboratory control samples, and spiked  samples  that  also  contain such surfactant) and  that all require- ments of paragraph (b)(1) and (b)(2) of this section are met. Samples having residual chlorine or other halogen must be dechlorinated prior to the ad- dition of such surfactant.

- The use of gas diffusion (using pH change to convert the analyte to gaseous form and/or heat to  separate an analyte contained in steam from the sample matrix) across a hydrophobic semi-permeable membrane to separate the analyte of interest from the sample matrix may be used in place of manual or automated  distillation in  methods for analysis such as ammonia, total cy- anide,  total  Kjeldahl  nitrogen,  and total phenols. These procedures do not replace the digestion procedures speci- fied in the approved methods and must be used in conjunction with those pro- cedures.

- Changes in equipment operating parameters such as the monitoring wavelength of a colorimeter or the re- action time and temperature as needed to  achieve  the  chemical  reactions  de-

fined in the unmodified CWA method. For example, molybdenum blue phos- phate methods have two absorbance maxima, one at about 660 nm and an- other at about 880 nm. The former is about 2.5 times less sensitive than the latter. Wavelength choice provides a cost-effective, dilution-free means to increase sensitivity  of  molybdenum blue phosphate methods.

- Interchange of oxidants, such as the use of titanium oxide in UV-as- sisted automated digestion of TOC and total phosphorus, as long as complete oxidation can be demonstrated.

(xxii) Use of an axially viewed torch with Method 200.7.

[77 FR 29810, May 18, 2012]

EDITORIAL  NOTE:  At  77  FR  29810,  May  18,

2012, § 136.6 was revised to include two para- graphs designated (b)(4)(xxii).

##### § 136.7   Quality  assurance  and  quality control.

The permittee/laboratory shall use suitable QA/QC procedures when con- ducting compliance analyses with any part 136 chemical method or an alter- native method specified by the permit- ting authority. These QA/QC proce- dures are generally included in the an- alytical method or may be part of the methods compendium  for  approved part 136 methods from a consensus or- ganization. For example, Standard Methods contains QA/QC procedures in the part 1000 section of the Standard Methods Compendium. The permittee/ laboratory shall follow these QA/QC procedures, as described in the method or methods compendium. If the method lacks QA/QC procedures, the permittee/ laboratory has the following options to comply with the QA/QC requirements:

- Refer to and follow the QA/QC published in the ‘‘equivalent’’ EPA method for that parameter that has such QA/QC procedures;

- Refer to the appropriate QA/QC section(s) of an approved part 136 meth- od from a consensus organization com- pendium;

(c)(1) Incorporate the following twelve quality control elements, where applicable, into the laboratory’s docu- mented standard operating procedure (SOP) for performing compliance anal- yses when using an approved part 136 method  when  the  method  lacks  such

#### Pt. 136, App. A, Meth. 601

QA/QC procedures. One or more of the twelve QC elements may not apply to a given method and may be omitted if a written rationale is provided indicating why the element(s) is/are inappropriate for a specific method.

  - Demonstration of Capability (DOC);

  - Method Detection Limit (MDL);

  - Laboratory reagent blank (LRB), also referred to as method blank (MB);

  - Laboratory fortified blank (LFB), also referred to as a spiked blank, or laboratory control sample (LCS);

  - Matrix spike (MS) and matrix spike duplicate (MSD), or laboratory fortified matrix (LFM) and LFM dupli- cate, may be used for suspected matrix interference problems to assess preci- sion;

  - Internal standards (for GC/MS analyses), surrogate standards (for or- ganic analysis) or tracers (for radiochemistry);

  - Calibration (initial and con- tinuing), also referred to as initial cali- bration verification (ICV) and con- tinuing calibration verification (CCV);

  - Control charts (or other trend analyses of quality control results);

  - Corrective action (root cause analysis);

  - QC acceptance criteria;

  - Definitions of preparation and analytical batches that may drive QC frequencies; and

  - Minimum frequency for con- ducting all QC elements.

- These twelve quality control ele- ments must be clearly documented in the written standard operating proce- dure for each analytical method not containing QA/QC procedures, where applicable.

[77 FR 29813, May 18, 2012]

APPENDIX A TO PART 136—METHODS FOR ORGANIC CHEMICAL ANALYSIS OF MUNICIPAL AND  INDUSTRIAL WASTE- WATER

METHOD 601—PURGEABLE HALOCARBONS

  - Scope and Application

  - This method covers the determination of 29 purgeable halocarbons.

The following parameters may be deter- mined by this method:

#### 40 CFR Ch. I (7–1–17 Edition)

| Parameter | STORET No. | CAS No. |
| --- | --- | --- |
| Bromodichloromethane ............... | 32101 | 75–27–4 |
| Bromoform .................................. | 32104 | 75–25–2 |
| Bromomethane ............................ | 34413 | 74–83–9 |
| Carbon tetrachloride ................... | 32102 | 56–23–5 |
| Chlorobenzene ............................ | 34301 | 108–90–7 |
| Chloroethane ............................... | 34311 | 75–00–3 |
| 2-Chloroethylvinyl ether .............. | 34576 | 100–75–8 |
| Chloroform .................................. | 32106 | 67–66–3 |
| Chloromethane ............................ | 34418 | 74–87–3 |
| Dibromochloromethane ............... | 32105 | 124–48–1 |
| 1,2-Dichlorobenzene ................... | 34536 | 95–50–1 |
| 1,3-Dichlorobenzene ................... | 34566 | 541–73–1 |
| 1,4-Dichlorobenzene ................... | 34571 | 106–46–7 |
| Dichlorodifluoromethane ............. | 34668 | 75–71–8 |
| 1,1-Dichloroethane ...................... | 34496 | 75–34–3 |
| 1,2-Dichloroethane ...................... | 34531 | 107–06–2 |
| 1,1-Dichloroethane ...................... | 34501 | 75–35–4 |
| trans-1,2-Dichloroethene ............. | 34546 | 156–60–5 |
| 1,2-Dichloropropane .................... | 34541 | 78–87–5 |
| cis-1,3-Dichloropropene .............. | 34704 | 10061–01–5 |
| trans-1,3-Dichloropropene .......... | 34699 | 10061–02–6 |
| Methylene chloride ...................... | 34423 | 75–09–2 |
| 1,1,2,2-Tetrachloroethane ........... | 34516 | 79–34–5 |
| Tetrachloroethene ....................... | 34475 | 127–18–4 |
| 1,1,1-Trichloroethane .................. | 34506 | 71–55–6 |
| 1,1,2-Trichloroethane .................. | 34511 | 79–00–5 |
| Tetrachloroethene ....................... | 39180 | 79–01–6 |
| Trichlorofluoromethane ............... | 34488 | 75–69–4 |
| Vinyl chloride ............................... | 39715 | 75–01–4 |

  - This is a purge and trap gas chromatographic (GC)  method  applicable  to the determination of the compounds listed above in municipal and  industrial  discharges as provided under 40 CFR 136.1. When this method is  used  to  analyze  unfamiliar  sam- ples for any or all of the compounds above, compound identifications should be sup- ported by at least one additional qualitative technique. This method describes analytical conditions for a second gas chromatographic column that can be used to confirm measure- ments made with the primary  column.  Meth- od 624 provides gas chromatograph/mass spectrometer (GC/MS) conditions  appro- priate for the qualitative and quantitative confirmation of results for most of the pa- rameters  listed  above.

  - The method detection limit (MDL, de- fined in Section 12.1) 1 for each parameter is listed in Table 1. The MDL for a specific wastewater may differ from those listed, de- pending upon the nature of interferences  in the sample matrix.

  - Any modification of this method,  be- yond those expressly permitted, shall be con- sidered as a major modification subject to application and approval of alternate test procedures under 40 CFR 136.4 and 136.5.

  - This method is restricted to use by or under the supervision of analysts experi- enced in the operation of a purge and trap system and a gas chromatograph and in the interpretation of gas chromatograms. Each analyst must demonstrate the ability to gen- erate acceptable results with this method using the procedure described in Section 8.2.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 601

  - Summary of Method

  - An inert gas is bubbled through a 5-mL water sample contained in a specially-de- signed purging chamber at ambient tempera- ture. The halocarbons are efficiently trans- ferred from the aqueous phase to the vapor phase. The vapor is swept through a sorbent trap where the halocarbons are trapped. After purging is completed, the trap is heat- ed and backflushed with the inert gas to desorb the halocarbons onto a gas chromatographic column. The gas chro- matograph is temperature programmed to separate the halocarbons which are then de- tected with a halide-specific detector. 2 3

  - The method provides an optional gas chromatographic column that may be help- ful in resolving the compounds of interest from interferences that may occur.

  - Interferences

  - Impurities in the purge gas and or- ganic compounds outgassing from the plumb- ing ahead of the trap account for the major- ity of contamination problems. The analyt- ical system must be demonstrated to be free from contamination under the conditions of the analysis by running laboratory reagent blanks as described in Section 8.1.3. The use of non-Teflon plastic tubing, non-Teflon thread sealants, or flow controllers with rub- ber components in the purge and trap system should be avoided.

  - Samples can be contaminated by diffu- sion of volatile organics (particularly fluoro- carbons and methylene chloride) through the septum seal ilto the sample during shipment and storage. A field reagent blank prepared from reagent water and carried through the sampling and handling protocol can serve as a check on such contamination.

  - Contamination by  carry-over  can occur whenever high level and low level sam- ples are sequentially analyzed. To reduce carry-over, the purging device and sample syringe must be rinsed with reagent water between sample analyses. Whenever an un- usually concentrated sample  is  encountered, it should be followed by an analysis of  rea- gent water to check for cross contamination. For samples containing large amounts of water-soluble materials, suspended solids, high boiling compounds or high organohalide levels, it may be necessary to wash out the purging device with a detergent  solution, rinse it with distilled water, and then dry it in a 105 C oven between analyses. The trap and other parts of the system are  also  sub- ject to contamination; therefore, frequent bakeout and purging of the entire system may be required.

  - Safety

  - The toxicity or carcinogenicity of each reagent used in this method has not been precisely defined; however, each chem-

ical compound should be treated as a poten- tial health hazard. From this viewpoint, ex- posure to these chemicals must be reduced to the lowest possible level by whatever means available. The laboratory is responsible for maintaining a current awareness file of OSHA regulations regarding the safe han- dling of the chemicals specified in this meth- od. A reference file of material data handling sheets should also be made available to all personnel involved in the chemical analysis. Additional references to laboratory safety are available and have been identified 4 6 for the information of the analyst.

  - The following parameters covered by this method have been  tentatively  classified as known or suspected, human or mamma- lian carcinogens: carbon tetrachloride, chlo- roform, 1,4-dichlorobenzene, and vinyl chlo- ride. Primary standards of these toxic com- pounds should be prepared in a hood. A NIOSH/MESA approved toxic gas respirator should be worn when the analyst handles high concentrations of these toxic com- pounds.

  - Apparatus and Materials

  - Sampling equipment, for discrete sam- pling.

    - Vial—25-mL capacity or larger, equipped with a screw cap with a hole in the center (Pierce #13075 or equivalent). Deter- gent wash, rinse with tap and distilled  water, and dry at 105 C before use.

    - Septum—Teflon-faced	silicone (Pierce #12722 or equivalent). Detergent wash, rinse with tap and distilled water, and dry at 105 C for 1 h before use.

  - Purge and trap system—The purge and trap system consists of three separate pieces of equipment: a purging device, trap, and desorber. Several complete systems are now commercially available.

    - The purging device must be designed to accept 5-mL samples with a water column at least 3 cm deep. The gaseous head space between the water column and the trap must have a total volume of less than 15 mL. The purge gas  must  pass through  the  water col- umn as finely divided bubbles with a diame- ter of less than 3 mm at the origin. The purge gas must be introduced no more than

5 mm from the base of the water  column. The purging device illustrated in Figure 1 meets these design criteria.

    - The trap must be at least 25 cm long and have an inside diameter of at least 0.105 in. The trap must be packed to contain the following minimum lengths of adsorbents: 1.0 cm of methyl silicone coated packing (Sec- tion 6.3.3), 7.7 cm of 2,6-diphenylene oxide polymer (Section 6.3.2), 7.7 cm of silica gel (Section 6.3.4), 7.7 cm of coconut charcoal (Section 6.3.1). If it is not necessary to ana- lyze for dichlorodifluoromethane, the char- coal can be eliminated, and the polymer sec- tion   lengthened   to   15   cm.   The   minimum

#### Pt. 136, App. A, Meth. 601

specifications for the trap are illustrated in Figure 2.

    - The desorber must be capable of rap- idly heating the trap to 180 C. The polymer section of  the trap  should not  be heated higher than 180 C and the remaining sec- tions should not exceed 200 C. The desorber illustrated in Figure 2 meets these design criteria.

    - The purge and trap system may be assembled as a separate unit or be coupled to a gas chromatograph as illustrated in Fig- ures 3 and 4.

  - Gas chromatograph—An analytical system complete  with  a  temperature  pro- grammable gas chromatograph suitable for on-column injection and all required acces- sories including syringes, analytical  col- umns, gases, detector, and strip-chart re- corder. A data system is recommended for measuring peak areas.

    - Column 1—8 ft long 0.1 in. ID stain-

less steel or glass, packed with 1% SP–1000 on Carbopack B (60/80 mesh) or equivalent. This column was used to develop the method performance statements in Section 12. Guidelines for the use of alternate column packings are provided in Section 10.1.

    - Column 2—6 ft long 0.1 in. ID stain-

less steel or glass, packed with chemically bonded n-octane on Porasil-C (100/120 mesh) or  equivalent.

    - Detector—Electrolytic   conductivity or microcoulometric detector. These types of detectors have proven effective in the anal- ysis of wastewaters for the parameters listed in the scope (Section 1.1). The electrolytic conductivity detector was used to develop the method performance statements in Sec- tion 12. Guidelines for the use of alternate detectors are provided in Section 10.1.

  - Syringes—5-mL glass hypodermic with Luerlok tip (two each), if applicable to the purging device.

  - Micro syringes—25-L, 0.006 in. ID nee-

dle.

  - Syringe valve—2-way, with Luer ends (three each).

  - Syringe—5-mL, gas-tight with shut-off valve.

  - Bottle—15-mL, screw-cap, with Teflon cap liner.

  - Balance—Analytical, capable of accu- rately weighing 0.0001 g.

  - Reagents

  - Reagent water—Reagent water is de- fined as a water in which an  interferent  is not observed at the  MDL  of  the  parameters of  interest.

    - Reagent water can be generated by passing tap water through a carbon filter bed containing about 1 lb of activated carbon (Filtrasorb-300, Calgon Corp., or equivalent).

    - A water  purification  system (Millipore Super-Q or equivalent)  may  be used to generate reagent water.

#### 40 CFR Ch. I (7–1–17 Edition)

    - Reagent water may also be prepared by boiling water for 15 min. Subsequently, while maintaining the temperature at 90 C, bubble a contaminant-free inert gas through the water for 1 h. While  still  hot,  transfer the water to a narrow mouth screw-cap bot- tle and  seal with  a  Teflon-lined septum  and cap.

  - Sodium thiosulfate—(ACS) Granular.

  - Trap Materials:

    - Coconut charcoal—6/10 mesh sieved to 26 mesh, Barnabey Cheney, CA–580–26 lot # M–2649 or equivalent.

    - 2,6-Diphenylene oxide polymer— Tenax, (60/80 mesh), chromatographic  grade or   equivalent.

    - Methyl silicone packing—3% OV–1 on Chromosorb-W (60/80 mesh) or equivalent.

    - Silica gel—35/60 mesh, Davison, grade-15 or equivalent.

  - Methanol—Pesticide quality or equiv- alent.

  - Stock standard solutions—Stock standard solutions may be prepared from pure standard materials or purchased as cer- tified solutions. Prepare stock standard solu- tions in methanol using assayed liquids or gases as appropriate. Because of the toxicity of some of the organohalides, primary dilu- tions of these materials should be prepared in a hood. A NIOSH/MESA approved toxic gas respirator should be used when the ana- lyst handles high concentrations of such ma- terials.

    - Place about  9.8  mL  of  methanol  into a 10-mL ground glass stoppered volumetric flask. Allow the flask to stand,  unstoppered, for about 10 min or until all alcohol wetted surfaces have dried. Weigh the flask to the learest 0.1 mg.

    - Add the assayed reference material:

      - Liquid—Using a 100 L syringe, im- mediately add two or more drops of assayed reference material to the flask, then re- weigh. Be sure that the drops fall directly into the alcohol without contacting the neck of the flask.

      - Gases—To prepare standards for any of the six halocarbons that boil below 30

C	(bromomethane,	chloroethane, chloromethane, dichlorodifluoromethane, trichlorofluoromethane,  vinyl   chloride),   fill a 5-mL valved gas-tight syringe with the ref- erence standard to the 5.0-mL mark.  Lower the needle to 5 mm above the methanol me- niscus. Slowly introduce the reference stand- ard above the surface of the liquid (the heavy gas  will  rapidly  dissolve  into  the  methanol).

    - Reweigh, dilute to volume, stopper, then mix by inverting the flask  several times. Calculate the concentration in g/L from the net gain in weight. When compound purity is assayed to be 96% or greater, the weight can be used without correction to cal- culate the concentration of the stock stand- ard. Commercially prepared stock standards can be used at any concentration if they are

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 601

certified  by  the  malufacturer  or  by  an  inde- pendent source.

    - Transfer the stock standard solution into a Teflon-sealed screw-cap bottle. Store, with minimal headspace, at ¥10 to ¥20 C and protect from light.

    - Prepare fresh standards weekly for the six gases and 2-chloroethylvinyl  ether. All other standards must be replaced after one month, or sooner if comparison with check standards indicates a problem.

  - Secondary dilution standards—Using stock standard solutions, prepare secondary dilution standards in methanol that contain the compounds of interest, either singly or mixed together. The secondary dilution standards should be prepared at concentra- tions such that the aqueous calibration standards prepared in Section 7.3.1 or 7.4.1 will bracket the working range of the ana- lytical system. Secondary dilution standards should be stored with minimal headspace and should be checked frequently for signs of degradation or evaporation, especially just prior to preparing calibration standards from them.

  - Quality control check sample con- centrate—See Section 8.2.1.

  - Calibration

  - Assemble a purge and trap system that meets the  specifications in  Section 5.2.  Con- dition the trap overnight at 180 C by backflushing with an inert gas flow of at least 20 mL/min. Condition the trap for 10 min once daily prior to use.

  - Connect the purge and trap system to a gas chromatograph. The gas chro- matograph must be operated using tempera- ture and flow rate conditions equivalent to those given in Table 1. Calibrate the purge and trap-gas chromatographic system using either the external standard technique (Sec- tion 7.3) or the internal standard technique (Section 7.4).

  - External  standard  calibration  proce-

7.3.1   Prepare  calibration  standards  at  a

centration in the standard. The results can be used to prepare a calibration curve for each compound. Alternatively, if the ratio of response to concentration (calibration fac- tor) is a constant over the working range (<10% relative standard deviation, RSD), lin- earity through the origin can be assumed and the average ratio or calibration factor can be used in place of a calibration curve.

  - Internal standard calibration proce- dure—To use this approach, the analyst must select one or more internal standards that are similar in analytical behavior to the compounds of interest. The analyst must fur- ther demonstrate that the measurement of the internal standard is not affected by method or matrix interferences. Because of these limitations, no internal standard  can be suggested that is applicable to all sam- ples. The compounds recommended for use as surrogate spikes in Section 8.7 have been used successfully as internal standards, be- cause of their generally unique retention times.

    - Prepare calibration standards at a minimum of three concentration levels for each parameter of interest as described in Section 7.3.1.

    - Prepare a spiking solution con- taining each of the internal standards  using the procedures described in Sections 6.5 and

6.6. It is recommended that the secondary di- lution standard be prepared at a concentra- tion of 15 g/mL of each internal standard compound. The addition of 10 L of this standard to 5.0 mL of sample or calibration standard would be equivalent to 30 g/L.

    - Analyze each calibration standard according to Section 10, adding 10 L of in- ternal  standard  spiking  solution  directly  to the syringe  (Section  10.4).  Tabulate  peak height or  area responses  against concentra- tion for each compound and internal stand- ard, and calculate response factors (RF) for each  compound  using  Equation  1.

		

## RF 

dure:

As    Cis

miminum  of  three  concentration  levels  for

each parameter by carefully adding 20.0 L of one or more secondary dilution standards to 100, 500, or 1000 L of reagent water. A 25-L syringe  with  a  0.006  in.  ID  needle  should  be

where:

Ais Cs 

Equation   1

used for this operation. One of the external standards should be at a concentration near, but above, the MDL (Table 1) and the other concentrations should correspond to the ex- pected range of concentrations found in real samples or should define the working range of the detector. These aqueous standards can be stored up to 24 h, if held in sealed vials with zero headspace as described in Section

9.2. If not so stored, they must be discarded after 1 h.

7.3.2 Analyze each calibration standard according to Section 10, and tabulate peak height   or   area   responses   versus   the   con-

As  = Response for the parameter to be meas-

ured.

Ais = Response for the internal standard.

Cis = Concentration of the internal standard.

Cs  = Concentration of the parameter to be measured.

If the RF value over the working range is a constant (<10% RSD), the RF can be assumed to be invariant and the average RF can be used for calculations. Alternatively, the re- sults can be used to plot a calibration curve of response ratios, As/Ais, vs. RF.

  - The  working  calibration  curve,  cali-

bration  factor,  or  RF  must  be  verified  on

#### Pt. 136, App. A, Meth. 601

each working day by the measurement of a QC check sample.

    - Prepare the QC check sample as de- scribed in Section 8.2.2.

    - Analyze the QC check sample accord- ing to Section 10.

    - For each parameter, compare the re- sponse (Q) with the corresponding calibra- tion acceptance criteria found in Table 2. If the responses for all parameters of interest fall within the designated ranges, analysis of actual samples can begin. If any individual Q falls outside the range, proceed according to Section 7.5.4.

NOTE: The large number of parameters in Table 2 present  a  substantial  probability that one or more will not meet the  calibra- tion acceptance criteria when all parameters are analyzed.

    - Repeat the test only for those pa- rameters that failed to meet the calibration acceptance criteria. If the response for a pa- rameter does not fall within the range  in this second test, a new calibration curve, calibration factor, or RF must be prepared for that parameter according to Section 7.3 or 7.4.

  - Quality Control

  - Each laboratory that uses this method is required to operate a formal quality  con- trol program. The minimum requirements of this program consist of an initial demonstra- tion of laboratory capability and an ongoing analysis of spiked samples to evaluate and document data quality. The laboratory must maintain records to document the quality of data that is generated. Ongoing data quality checks are compared with established per- formance criteria to determine if the results of analyses meet the performance character- istics of the method. When results of sample spikes indicate atypical method perform- ance, a quality control check  standard  must be analyzed to confirm that the measure- ments were performed in an in-control mode of operation.

    - The analyst must make an initial, one-time, demonstration of the ability to generate acceptable accuracy and precision with this method. This  ability  is  established as described in Section 8.2.

    - In recognition of advances that are occurring in chromatography, the analyst is permitted certain  options  (detailed  in  Sec- tion 10.1) to improve the separations or lower the cost of measurements. Each time such a modification is made to the method, the ana- lyst is required to repeat the procedure in Section 8.2.

    - Each day, the analyst must analyze a reagent water blank to demonstrate that interferences from the analytical system are under control.

    - The laboratory must, on an ongoing basis, spike and analyze a minimum of 10% of all samples to monitor and evaluate lab-

#### 40 CFR Ch. I (7–1–17 Edition)

oratory data quality. This procedure is de- scribed in Section 8.3.

    - The laboratory must, on an ongoing basis, demonstrate through the analyses of quality control  check standards  that  the op- eration of the measurement system is in con- trol.  This  procedure  is  described  in  Section

8.4. The frequency of the check standard analyses is equivalent to 10% of all samples analyzed but may be reduced if spike recov- eries from samples (Section 8.3) meet all specified quality control criteria.

    - The laboratory must maintain per- formance records to document the quality of data that is generated. This procedure is de- scribed in Section 8.5.

  - To establish the ability to generate acceptable accuracy and precision, the ana- lyst must perform the following operations.

    - A quality control (QC) check sample concentrate is required containing each pa- rameter of  interest  at a  concentration  of  10

g/mL in methanol. The QC check sample concentrate must be obtained from the U.S. Environmental Protection Agency, Environ- mental Monitoring and Support Laboratory in Cincinnati, Ohio, if available. If not avail- able from that source, the QC check sample concentrate must be obtained from another external source. If not available from either source above, the QC check sample con- centrate must be prepared by the laboratory using stock standards prepared independ- ently from those used for calibration.

    - Prepare a QC check sample to con- tain 20 g/L of each parameter by adding 200

L of QC check sample concentrate to 100 mL

of reagent water.

    - Analyze four 5-mL aliquots of the well-mixed QC check sample according to Section 10.

    - Calculate the average recovery (X¯ ) in

g/L, and the standard deviation of the re- covery (s) in g/L, for each parameter of in- terest using the four results.

    - For each parameter compare s and X¯

with  the  corresponding  acceptance  criteria

for precision and accuracy, respectively, found in Table 2. If s and X¯  for all param-

eters of interest meet the acceptance cri- teria, the system performance is acceptable and analysis of actual samples can begin. If any individual s exceeds the precision limit

or any individual X¯  falls outside the range

for accuracy, then the system performance is unacceptable for that parameter.

NOTE: The large number of parameters in Table 2 present  a  substantial  probability that one or more will fail at least one of the acceptance criteria when all parameters are analyzed.

    - When one or more of the parameters tested fail at least one of the acceptance cri- teria, the analyst must proceed according to Section 8.2.6.1 or 8.2.6.2.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 601

      - Locate and correct the source of the problem and repeat the test for all pa- rameters of interest beginning with Section 8.2.3.

      - Beginning with Section 8.2.3, repeat the test only for those  parameters  that failed to meet criteria. Repeated failure, however, will confirm a  general  problem with the measurement system. If this occurs, locate and correct the source of the problem and repeat the test for all compounds of in- terest beginning with Section 8.2.3.

  - The laboratory must, on an ongoing basis, spike at least 10% of the samples from each sample site being monitored to assess accuracy. For laboratories analyzing one to ten samples per month, at least one spiked sample per month is required.

    - The concentration of the spike in the sample should be determined as follows:

      - If, as in compliance monitoring, the concentration of a specific parameter in the sample is being checked against a regu- latory concentration limit, the spike should be at that limit or 1 to 5 times higher than the background concentration determined in Section 8.3.2, whichever concentration would be larger.

      - If the concentration of a specific parameter in the sample  is  not  being checked against a limit specific to that pa- rameter, the spike should be at 20 g/L or 1 to 5  times  higher than  the  background  con- centration determined in Section 8.3.2, whichever concentration would be larger.

    - Analyze one 5-mL sample aliquot to determine the background concentration (B) of each parameter. If necessary, prepare a new QC check sample concentrate (Section 8.2.1) appropriate for the background con- centrations in the sample. Spike a second 5- mL sample aliquot with 10 L of the QC check sample concentrate and analyze it to determine   the   concentration   after   spiking

(A) of each parameter. Calculate each per- cent recovery (P) as 100(A¥B)%/T, where T is the known true value of the spike.

    - Compare the percent recovery (P) for each parameter with the corresponding QC acceptance criteria found in Table 2. These acceptance criteria were calculated to in- clude an allowance for error in measurement of both the background and spike concentra- tions, assuming a spike  to  background  ratio of 5:1. This error will be accounted for to the extent that the analyst’s spike to back- ground ratio approaches 5:1. 7 If spiking was performed at a concentration lower than 20

g/L, the analyst must use either the QC ac- ceptance criteria in Table 2, or optional QC acceptance criteria calculated  for the  spe- cific spike concentration. To calculate op- tional acceptance criteria for the recovery of a parameter: (1) Calculate accuracy (X) using the equation in Table 3,  substituting the spike concentration (T) for C; (2) cal- culate  overall  precision  (S)  using  the  equa-

tion in Table 3, substituting Xfor X¯ ; (3) cal- culate the range for recovery at the spike concentration as (100 X/T)2.44(100 S/T)%. 7

    - If any individual P falls outside the designated range for recovery, that param- eter has failed the acceptance criteria. A check standard containing each parameter that failed the criteria must be analyzed as described in Section 8.4.

  - If any parameter fails the acceptance criteria for recovery in Section 8.3, a QC check standard containing each parameter that failed must be prepared and analyzed.

NOTE: The frequency for the required anal- ysis of a QC check standard will depend upon the number of parameters being simulta- neously tested, the complexity of the sample matrix, and the performance of the labora- tory. If the entire list of parameters in Table 2 must be measured in the sample in Section 8.3, the probability that the analysis of a QC check standard will be required is high.  In this case the QC check standard should be routinely analyzed with the spiked sample.

    - Prepare the QC check standard by adding 10 L of QC check sample concentrate (Section 8.2.1 or 8.3.2) to 5 mL of reagent water. The QC check standard needs only to contain  the  parameters  that   failed   criteria in the  test in  Section 8.3.

    - Analyze the QC check standard to determine the concentration measured (A) of each parameter. Calculate each percent re- covery (Ps) as 100 (A/T)%, where T is the true value of the standard concentration.

    - Compare the percent recovery (Ps) for each parameter with the corresponding QC acceptance criteria found in Table 2. Only parameters that failed the test in Section 8.3 need to be compared with these  criteria.  If the recovery of any such parameter falls out- side the designated range, the laboratory performance for that parameter is judged to be out of control, and the problem must be immediately identified and corrected. The analytical result for that parameter in the unspiked sample is suspect  and may not  be reported for regulatory compliance purposes.

  - As part of the QC program for the lab- oratory, method accuracy for wastewater samples must be assessed and records must be maintained. After the analysis of five spiked wastewater samples as in Section 8.3,

calculate  the  average  percent  recovery  (P¯ )

and the standard deviation of the percent re- covery (sp). Express the accuracy assessment

as a percent recovery interval from P¯ ¥2sp to P¯  + 2sp. If p¯ = 90% and sp = 10%, for example,

the accuracy interval is expressed as 70– 110%. Update the accuracy  assessment  for each parameter on a regular basis (e.g. after each five to  ten  new  accuracy  measure- ments).

  - It is recommended that the laboratory adopt additional quality assurance practices for use with this method. The specific prac- tices that are most productive depend upon

#### Pt. 136, App. A, Meth. 601

the needs of the laboratory and the nature of the samples. Field duplicates may be ana- lyzed to assess the precision of the environ- mental measurements. When doubt exists over the identification of a peak on the chro- matogram, confirmatory techniques such as gas chromatography with a dissimilar col- umn, specific element detector, or mass spectrometer must be used. Whenever pos- sible, the laboratory should analyze standard reference materials and participate in rel- evant performance evaluation studies.

  - The analyst should monitor both the performance  of  the  analytical  system  and the effectiveness of the method in dealing with each sample matrix by spiking each sample, standard, and reagent water blank with surrogate halocarbons. A  combination of	bromochloromethane,	2-bromo-1- chloropropane, and 1,4-dichlorobutane is rec- ommended to encompass the range of the temperature program used in this method. From stock standard solutions  prepared  as in Section 6.5, add a volume to give 750 g of each surrogate to 45 mL of reagent water contained in a 50-mL volumetric flask, mix and dilute to volume for  a  concentration  of 15 ng/L. Add 10 L of this surrogate spiking solution directly into the 5-mL syringe with every sample and reference standard ana- lyzed. Prepare a fresh surrogate spiking solu- tion on a weekly basis. If the internal stand- ard calibration procedure is being used, the surrogate compounds may be added directly to the internal standard spiking solution (Section 7.4.2).

  - Sample Collection, Preservation, and Handling

  - All samples must be iced or  refrig- erated from the time of collection until anal- ysis. If the sample contains free or combined chlorine,  add  sodium   thiosulfate   preserva- tive (10 mg/40 mL is sufficient for up to  5 ppm Cl2) to  the  empty  sample  bottle  just prior to shipping to the sampling site. EPA Methods 330.4 and 330.5 may be used for measurement  of   residual   chlorine. 8   Field test  kits  are  available  for  this  purpose.

  - Grab samples must be collected in glass containers having a total volume of at least 25 mL. Fill the sample bottle just to overflowing in such a manner that no air bubbles pass through the sample as the bot- tle is being filled. Seal the bottle so that no air bubbles are entrapped in it. If preserva- tive has been added, shake vigorously for 1 min. Maintain the hermetic seal on the sam- ple bottle until time of analysis.

  - All samples must be analyzed  within 14 days of collection. 3

  - Procedure

10.1 Table 1 summarizes the recommended operating conditions for the gas chro- matograph.   Included   in   this   table   are   esti-

#### 40 CFR Ch. I (7–1–17 Edition)

mated retention times and MDL that can be achieved under these conditions. An example of the separations achieved by Column 1 is shown in Figure 5. Other packed columns, chromatographic conditions,  or  detectors may  be  used  if  the  requirements  of  Section

8.2 are met.

  - Calibrate the system daily as de- scribed in Section 7.

  - Adjust the purge gas (nitrogen or he- lium) flow rate to 40 mL/min. Attach the trap inlet to the purging device, and set the purge and trap system to purge (Figure 3). Open the syringe valve located on the purg- ing device sample introduction needle.

  - Allow the sample to come to ambient temperature prior to introducing it to the syringe. Remove the plunger from a 5-mL sy- ringe and attach a closed syringe valve. Open the sample bottle (or standard) and carefully pour the sample into the syringe barrel  to just short of overflowing. Replace the sy- ringe plunger and compress the sample. Open the syringe valve and vent any residual air while adjusting the sample volume to 5.0 mL. Since this process of taking an aliquot de- stroys the validity of the sample for future analysis, the analyst should fill a second sy- ringe at this time to protect against possible loss of data. Add 10.0 L of the surrogate spiking solution (Section 8.7) and 10.0 L of the internal standard spiking solution (Sec- tion 7.4.2), if applicable, through the valve bore, then close the valve.

  - Attach the syringe-syringe valve as- sembly to the syringe valve on the purging device. Open the syringe valves and  inject the sample into the purging chamber.

  - Close both valves and purge the sam- ple for 11.0 0.1 min at ambient temperature.

  - After the 11-min purge time, attach the trap to the chromatograph, adjust the purge and trap system to the desorb mode (Figure 4), and begin to temperature pro- gram the gas chromatograph. Introduce the trapped materials to the GC column by rap- idly heating the trap to 180 C while backflushing the trap with an inert gas be- tween 20 and 60 mL/min for 4 min. If rapid heating of the trap cannot be achieved, the GC column must be used as a secondary trap by cooling it to 30 C (subambient tempera- ture, if poor peak geometry or random reten- tion time problems persist) instead of the initial program temperature of 45 C

  - While the trap is being desorbed into the gas chromatograph, empty the purging chamber using the sample introduction sy- ringe. Wash the chamber with two 5-mL flushes of reagent water.

  - After desorbing the sample for 4 min, recondition the trap by returning the purge and trap system to the purge mode. Wait 15 s then close the syringe valve on the purging device to begin gas flow through the trap. The trap temperature should  be  maintained at 180 C After approximately 7 min, turn off

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 601

the trap heater and open the syringe valve to stop the gas flow through the trap. When the trap is cool, the next sample can be ana- lyzed.

  - Identify the parameters in the sam- ple by comparing the retention times of the peaks in the sample chromatogram with those of the peaks in standard chromatograms. The width of the retention time window used to make identifications should be based upon measurements of ac- tual retention time variations of standards over the course of a day. Three times the standard deviation of a retention time for a compound can be used to calculate a sug- gested window size; however, the experience of the analyst should weigh heavily in the interpretation of chromatograms.

  - If the  response  for a  peak  exceeds the working range of the system, prepare a dilution of the sample with reagent water from the aliquot in the second syringe and reanalyze.

  - Calculations

  - Determine the concentration of indi- vidual compounds in the sample.

    - If the external standard calibration procedure is used, calculate the concentra- tion of the parameter being measured from the peak response using the calibration curve or calibration factor determined in Section 7.3.2.

    - If the internal standard calibration procedure is used, calculate the concentra- tion in the sample using the response factor (RF) determined in Section 7.4.3 and Equa- tion 2.

Equation   2

As Cis 

## Concentration (g/L) 

Ais RF

where:

As  = Response for the parameter to be meas- ured.

Ais = Response for the internal standard.

Cis = Concentration of the internal standard.

11.2 Report results in g/L without correc- tion for recovery data. All QC data obtained should be reported with the sample results.

  - Method Performance

  - The method detection limit (MDL) is defined as the minimum concentration of a substance that can be measured and reported with 99% confidence that the value is above zero. 1  The  MDL  concentration  listed   in Table 1 were obtained using reagent water. 11. Similar results were achieved using rep- resentative wastewaters. The MDL actually achieved in a given analysis will vary de- pending on instrument sensitivity and ma- trix  effects.

  - This method is recommended for use in the concentration range from the MDL to 1000 MDL. Direct aqueous injection tech- niques should be used to measure concentra- tion levels above 1000 MDL.

  - This method was tested by 20 labora- tories using reagent water, drinking water, surface water, and three industrial wastewaters spiked at six concentrations over the range 8.0 to 500 g/L. 9 Single oper- ator precision, overall precision, and method accuracy were found to be directly related to the concentration of the parameter and es- sentially independent of the sample matrix. Linear equations to describe these relation- ships are presented in Table 3.

References

- 40 CFR part 136, appendix B.

- Bellar,  T.A.,  and  Lichtenberg,  J.J. ‘‘De- termining   Volatile   Organics   at   Microgram- per-Litre-Levels   by   Gas   Chromatography,’’ Journal of the American Water Works Associa- tion, 66, 739 (1974).

- Bellar, T.A., and Lichtenberg, J.J. ‘‘Semi-Automated Headspace Analysis of Drinking Waters and Industrial Waters for Purgeable Volatile Organic Compounds,’’ Proceedings from Symposium on Measure- ment of Organic Pollutants in Water and Wastewater, American Society for Testing and Materials, STP 686, C.E. Van  Hall,  edi- tor, 1978.

- ‘‘Carcinogens—Working With Carcino- gens,’’ Department of Health, Education, and Welfare, Public Health Service, Center for Disease Control, National Institute for Occu- pational Safety and Health, Publication No. 77–206, August 1977.

- ‘‘OSHA Safety and Health Standards, General Industry’’ (29 CFR part 1910), Occu- pational Safety and Health Administration, OSHA 2206 (Revised, January 1976).

- ‘‘Safety in Academic Chemistry Labora- tories,’’ American Chemical Society Publica- tion, Committee on Chemical Safety, 3rd Edition, 1979.

- Provost,  L.P.,  and  Elder,  R.S.  ‘‘Interpre- tation   of   Percent   Recovery   Data,’’   American Laboratory, 15, 58–63  (1983).  (The  value  2.44 used  in  the  equation  in  Section  8.3.3  is  two times the value 1.22 derived in this report.)

- ‘‘Methods 330.4 (Titrimetric, DPD-FAS) and 330.5 (Spectrophotometric, DPD) for Chlorine, Total Residual,’’ Methods for Chemical Analysis of Water and Wastes, EPA 600/4–79–020, U.S. Environmental Protection Agency, Environmental Monitoring and Sup- port Laboratory, Cincinnati, Ohio  45268, March 1979.

- ‘‘EPA Method Study 24, Method 601— Purgeable Halocarbons by the Purge and Trap Method,’’ EPA 600/4–84–064, National Technical Information Service, PB84–212448, Springfield, Virginia 22161, July 1984.

- ‘‘Method Validation Data for EPA Method 601,’’ Memorandum from B. Potter,

#### Pt. 136, App. A, Meth. 601

U.S. Environmental  Protection  Agency,  En- vironmental Monitoring and Support Lab- oratory, Cincinnati, Ohio 45268, November 10, 1983.

#### 40 CFR Ch. I (7–1–17 Edition)

- Bellar, T. A., Unpublished data, U.S. Environmental Protection Agency, Environ- mental Monitoring and Support Laboratory, Cincinnati, Ohio 45268, 1981.

TABLE 1—CHROMATOGRAPHIC CONDITIONS AND METHOD DETECTION LIMITS

| Parameter | Retention time (min) | Method detection limit (g/L) |
| --- | --- | --- |
|  | Column 1 | Column 2 |  |
| Chloromethane ................................................................................ | 1.50 | 5.28 | 0.08 |
| Bromomethane ................................................................................ | 2.17 | 7.05 | 1.18 |
| Dichlorodifluoromethane .................................................................. | 2.62 | nd | 1.81 |
| Vinyl chloride ................................................................................... | 2.67 | 5.28 | 0.18 |
| Chloroethane ................................................................................... | 3.33 | 8.68 | 0.52 |
| Methylene chloride .......................................................................... | 5.25 | 10.1 | 0.25 |
| Trichlorofluoromethane .................................................................... | 7.18 | nd | nd |
| 1,1-Dichloroethene .......................................................................... | 7.93 | 7.72 | 0.13 |
| 1,1-Dichloroethane .......................................................................... | 9.30 | 12.6 | 0.07 |
| trans-1,2-Dichloroethene ................................................................. | 10.1 | 9.38 | 0.10 |
| Chloroform ....................................................................................... | 10.7 | 12.1 | 0.05 |
| 1,2-Dichloroethane .......................................................................... | 11.4 | 15.4 | 0.03 |
| 1,1,1-Trichloroethane ...................................................................... | 12.6 | 13.1 | 0.03 |
| Carbon tetrachloride ........................................................................ | 13.0 | 14.4 | 0.12 |
| Bromodichloromethane ................................................................... | 13.7 | 14.6 | 0.10 |
| 1,2-Dichloropropane ........................................................................ | 14.9 | 16.6 | 0.04 |
| cis-1,3-Dichloropropene .................................................................. | 15.2 | 16.6 | 0.34 |
| Trichloroethene ................................................................................ | 15.8 | 13.1 | 0.12 |
| Dibromochloromethane ................................................................... | 16.5 | 16.6 | 0.09 |
| 1,1,2-Trichloroethane ...................................................................... | 16.5 | 18.1 | 0.02 |
| trans-1,3-Dichloropropene ............................................................... | 16.5 | 18.0 | 0.20 |
| 2-Chloroethylvinyl ether ................................................................... | 18.0 | nd | 0.13 |
| Bromoform ....................................................................................... | 19.2 | 19.2 | 0.20 |
| 1,1,2,2-Tetrachloroethane ............................................................... | 21.6 | nd | 0.03 |
| Tetrachloroethene ........................................................................... | 21.7 | 15.0 | 0.03 |
| Chlorobenzene ................................................................................ | 24.2 | 18.8 | 0.25 |
| 1,3-Dichlorobenzene ....................................................................... | 34.0 | 22.4 | 0.32 |
| 1,2-Dichlorobenzene ....................................................................... | 34.9 | 23.5 | 0.15 |
| 1,4-Dichlorobenzene ....................................................................... | 35.4 | 22.3 | 0.24 |

Column 1 conditions: Carbopack B (60/80 mesh) coated with 1% SP–1000 packed in an 8 ft 0.1 in. ID stainless steel or glass column with helium carrier gas at 40 mL/min flow rate. Column temperature held at 45 C for 3 min then programmed at 8

C/min to 220 C and held for 15 min.

Column 2 conditions: Porisil-C (100/120 mesh) coated with n-octane packed in a 6 ft 0.1 in. ID stainless steel or glass col- umn with helium carrier gas at 40 mL/min flow rate. Column temperature held at 50 C for 3 min then programmed at 6 C/min to 170 C and held for 4 min.

nd = not determined.

TABLE 2—CALIBRATION AND QC ACCEPTANCE CRITERIA—METHOD 601 A

| Parameter | Range for Q (g/L) | Limit for s (g/L) | Range for X¯ (g/L) | Range P, Ps (%) |
| --- | --- | --- | --- | --- |
| Bromodichloromethane ..................................................................... | 15.2–24.8 | 4.3 | 10.7–32.0 | 42–172 |
| Bromoform ......................................................................................... | 14.7–25.3 | 4.7 | 5.0–29.3 | 13–159 |
| Bromomethane .................................................................................. | 11.7–28.3 | 7.6 | 3.4–24.5 | D–144 |
| Carbon tetrachloride .......................................................................... | 13.7–26.3 | 5.6 | 11.8–25.3 | 43–143 |
| Chlorobenzene .................................................................................. | 14.4–25.6 | 5.0 | 10.2–27.4 | 38–150 |
| Chloroethane ..................................................................................... | 15.4–24.6 | 4.4 | 11.3–25.2 | 46–137 |
| 2-Chloroethylvinyl ether .................................................................... | 12.0–28.0 | 8.3 | 4.5–35.5 | 14–186 |
| Chloroform ......................................................................................... | 15.0–25.0 | 4.5 | 12.4–24.0 | 49–133 |
| Chloromethane .................................................................................. | 11.9–28.1 | 7.4 | D–34.9 | D–193 |
| Dibromochloromethane ..................................................................... | 13.1–26.9 | 6.3 | 7.9–35.1 | 24–191 |
| 1,2-Dichlorobenzene ......................................................................... | 14.0–26.0 | 5.5 | 1.7–38.9 | D–208 |
| 1,3-Dichlorobenzene ......................................................................... | 9.9–30.1 | 9.1 | 6.2–32.6 | 7–187 |
| 1,4-Dichlorobenzene ......................................................................... | 13.9–26.1 | 5.5 | 11.5–25.5 | 42–143 |
| 1,1-Dichloroethane ............................................................................ | 16.8–23.2 | 3.2 | 11.2–24.6 | 47–132 |
| 1,2-Dichloroethane ............................................................................ | 14.3–25.7 | 5.2 | 13.0–26.5 | 51–147 |
| 1,1-Dichloroethene ............................................................................ | 12.6–27.4 | 6.6 | 10.2–27.3 | 28–167 |
| trans-1,2-Dichloroethene ................................................................... | 12.8–27.2 | 6.4 | 11.4–27.1 | 38–155 |
| 1,2-Dichloropropane .......................................................................... | 14.8–25.2 | 5.2 | 10.1–29.9 | 44–156 |
| cis-1,3-Dichloropropene .................................................................... | 12.8–27.2 | 7.3 | 6.2–33.8 | 22–178 |
| trans-1,3-Dichloropropene ................................................................. | 12.8–27.2 | 7.3 | 6.2–33.8 | 22–178 |
| Methylene chloride ............................................................................ | 15.5–24.5 | 4.0 | 7.0–27.6 | 25–162 |
| 1,1,2,2-Tetrachloroethane ................................................................. | 9.8–30.2 | 9.2 | 6.6–31.8 | 8–184 |
| Tetrachloroethene ............................................................................. | 14.0–26.0 | 5.4 | 8.1–29.6 | 26–162 |

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 601

TABLE 2—CALIBRATION AND QC ACCEPTANCE CRITERIA—METHOD 601 A—Continued

| Parameter | Range for Q (g/L) | Limit for s (g/L) | Range for X¯ (g/L) | Range P, Ps (%) |
| --- | --- | --- | --- | --- |
| 1,1,1-Trichloroethane ........................................................................ | 14.2–25.8 | 4.9 | 10.8–24.8 | 41–138 |
| 1,1,2-Trichloroethane ........................................................................ | 15.7–24.3 | 3.9 | 9.6–25.4 | 39–136 |
| Trichloroethene ................................................................................. | 15.4–24.6 | 4.2 | 9.2–26.6 | 35–146 |
| Trichlorofluoromethane ..................................................................... | 13.3–26.7 | 6.0 | 7.4–28.1 | 21–156 |
| Vinyl chloride ..................................................................................... | 13.7–26.3 | 5.7 | 8.2–29.9 | 28–163 |

a Criteria were calculated assuming a QC check sample concentration of 20 g/L. Q = Concentration measured in QC check sample, in g/L (Section 7.5.3).

s = Standard deviation of four recovery measurements, in g/L (Section 8.2.4). X¯ = Average recovery for four recovery measurements, in g/L (Section 8.2.4).

P, Ps  = Percent recovery measured (Section 8.3.2, Section 8.4.2). D = Detected; result must be greater than zero.

NOTE: These criteria are based directly upon the method performance data in Table 3. Where necessary, the limits for recov- ery have been broadened to assure applicability of the limits to concentrations below those used to develop Table 3.

TABLE 3—METHOD ACCURACY AND PRECISION AS FUNCTIONS OF CONCENTRATION—METHOD 601

| Parameter | Accuracy, as re- covery, X(g/L) | Single analyst pre- cision, sr(g/L) | Overall precision, S(g/L) |
| --- | --- | --- | --- |
| Bromodichloromethane ................................................................... | 1.12C¥1.02 | 0.11X¯ + 0.04 | 0.20X¯ + 1.00 |
| Bromoform ....................................................................................... | 0.96C¥2.05 | 0.12X¯ + 0.58 | 0.21X¯ + 2.41 |
| Bromomethane ................................................................................ | 0.76C¥1.27 | 0.28X¯ + 0.27 | 0.36X¯ + 0.94 |
| Carbon tetrachloride ........................................................................ | 0.98C¥1.04 | 0.15X¯ + 0.38 | 0.20X¯ + 0.39 |
| Chlorobenzene ................................................................................ | 1.00C¥1.23 | 0.15X¯ ¥0.02 | 0.18X¯ + 1.21 |
| Choroethane .................................................................................... | 0.99C¥1.53 | 0.14X¯ ¥0.13 | 0.17X¯ + 0.63 |
| 2-Chloroethylvinyl ether a ................................................................ | 1.00C | 0.20X¯ | 0.35X¯ |
| Chloroform ....................................................................................... | 0.93C¥0.39 | 0.13X¯ + 0.15 | 0.19X¯ ¥0.02 |
| Chloromethane ................................................................................ | 0.77C + 0.18 | 0.28X¯ ¥0.31 | 0.52X¯ + 1.31 |
| Dibromochloromethane ................................................................... | 0.94C + 2.72 | 0.11X¯ + 1.10 | 0.24X¯ + 1.68 |
| 1,2-Dichlorobenzene ....................................................................... | 0.93C + 1.70 | 0.20X¯ + 0.97 | 0.13X¯ + 6.13 |
| 1,3-Dichlorobenzene ....................................................................... | 0.95C + 0.43 | 0.14X¯ + 2.33 | 0.26X¯ + 2.34 |
| 1,4-Dichlorobenzene ....................................................................... | 0.93C¥0.09 | 0.15X¯ + 0.29 | 0.20X¯ + 0.41 |
| 1,1-Dichloroethane .......................................................................... | 0.95C¥1.08 | 0.09X¯ + 0.17 | 0.14X¯ + 0.94 |
| 1,2-Dichloroethane .......................................................................... | 1.04C¥1.06 | 0.11X¯ + 0.70 | 0.15X¯ + 0.94 |
| 1,1-Dichloroethene .......................................................................... | 0.98C¥0.87 | 0.21X¯ ¥0.23 | 0.29X¯ ¥0.40 |
| trans-1,2-Dichloroethene ................................................................. | 0.97C¥0.16 | 0.11X¯ + 1.46 | 0.17X¯ + 1.46 |
| 1,2-Dichloropropane a ..................................................................... | 1.00C | 0.13X¯ | 0.23X¯ |
| cis-1,3-Dichloropropene a ................................................................ | 1.00C | 0.18X¯ | 0.32X¯ |
| trans-1,3-Dichloropropene a ............................................................ | 1.00C | 0.18X¯ | 0.32X¯ |
| Methylene chloride .......................................................................... | 0.91C¥0.93 | 0.11X¯ + 0.33 | 0.21X¯ + 1.43 |
| 1,1,2,2-Tetrachloroethene ............................................................... | 0.95C + 0.19 | 0.14X¯ + 2.41 | 0.23X¯ + 2.79 |
| Tetrachloroethene ........................................................................... | 0.94C + 0.06 | 0.14X¯ + 0.38 | 0.18X¯ + 2.21 |
| 1,1,1-Trichloroethane ...................................................................... | 0.90C¥0.16 | 0.15X¯ + 0.04 | 0.20X¯ + 0.37 |
| 1,1,2-Trichloroethane ...................................................................... | 0.86C + 0.30 | 0.13X¯ ¥0.14 | 0.19X¯ + 0.67 |
| Trichloroethene ................................................................................ | 0.87C + 0.48 | 0.13X¯ ¥0.03 | 0.23X¯ + 0.30 |
| Trichlorofluoromethane .................................................................... | 0.89C¥0.07 | 0.15X¯ + 0.67 | 0.26X¯ + 0.91 |
| Vinyl chloride ................................................................................... | 0.97C¥0.36 | 0.13X¯ + 0.65 | 0.27X¯ + 0.40 |

X¯ = Expected recovery for one or more measurements of a sample containing a concentration of C, in g/L.

sn= Expected single analyst standard deviation of measurements at an average concentration found of X¯ , in g/L. S1 = Expected interlaboratory standard deviation of measurements at an average concentration found of X¯ , in g/L. C = True value for the concentration, in g/L.

X¯ = Average recovery found for measurements of samples containing a concentration of C, in g/L.

a Estimates based upon the performance in a single laboratory. 10

#### Pt. 136, App. A, Meth. 601

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 601

Pt. 136, App. A, Meth. 601

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 601

Pt. 136, App. A, Meth. 602

METHOD 602—PURGEABLE AROMATICS

- Scope and Application

  - This method covers the determination of various purgeable aromatics. The fol- lowing parameters may be determined by this method:

| Parameter | STORET No. | CAS No. |
| --- | --- | --- |
| Benzene .......................................... | 34030 | 71–43–2 |
| Chlorobenzene ................................ | 34301 | 108–90–7 |
| 1,2-Dichlorobenzene ....................... | 34536 | 95–50–1 |
| 1,3-Dichlorobenzene ....................... | 34566 | 541–73–1 |
| 1,4-Dichlorobenzene ....................... | 34571 | 106–46–7 |
| Ethylbenzene .................................. | 34371 | 100–41–4 |
| Toluene ........................................... | 34010 | 108–88–3 |

  - This is a purge and trap gas chromatographic (GC)  method  applicable  to the determination of the compounds listed above in municipal and  industrial  discharges as provided under 40 CFR 136.1. When this method is  used  to  analyze  unfamiliar  sam- ples for any or all of the compounds above, compound identifications should be sup- ported by at least one additional qualitative technique. This method describes analytical conditions for a second gas chromatographic column that can be used to confirm measure- ments made with the primary  column.  Meth- od 624 provides gas chromatograph/mass spectrometer (GC/MS) conditions  appro- priate for the qualitative and quantitative confirmation of results for all of the param- eters  listed  above.

  - The method detection limit (MDL, de- fined in Section 12.1) 1 for each parameter is listed in Table 1. The MDL for a specific wastewater may differ from those listed, de- pending upon the nature of interferences  in the sample matrix.

  - Any modification of this method,  be- yond those expressly permitted, shall be con- sidered as a major modification subject to application and approval of alternate test procedures under 40 CFR 136.4 and 136.5.

  - This method is restricted to use by or under the supervision of analysts experi- enced in the operation of a purge and trap system and a gas chromatograph and in the interpretation of gas chromatograms. Each analyst must demonstrate the ability to gen- erate acceptable results with this method using the procedure described in Section 8.2.

- Summary of Method

  - An inert gas is bubbled through a 5-mL water sample contained in a specially-de- signed purging chamber at ambient tempera- ture. The aromatics are efficiently trans- ferred from the aqueous phase to the vapor phase. The vapor is swept through a sorbent trap where the aromatics are trapped. After purging is completed, the trap is heated and backflushed with the inert gas to desorb the aromatics onto a gas chromatographic col-

#### 40 CFR Ch. I (7–1–17 Edition)

umn. The gas chromatograph is temperature programmed to separate the aromatics which are then detected with a photoionization detector. 2 3

  - The method provides an optional gas chromatographic column that may be help- ful in resolving the compounds of interest from interferences that may occur.

- Interferences

  - Impurities in the purge gas and or- ganic compounds outgassing from the plumb- ing ahead of the trap account for the major- ity of contamination problems. The analyt- ical system must be demonstrated to be free from contamination under the conditions of the analysis by running laboratory reagent blanks as described in Section 8.1.3. The use of non-Teflon plastic tubing, non-Teflon thread sealants, or flow controllers with rub- ber components in the purge and trap system should be avoided.

  - Samples can be contaminated by diffu- sion of volatile organics through the septum seal into the sample during shipment and storage. A field reagent blank prepared from reagent water and carried through the sam- pling and handling protocol can serve as a check on such contamination.

  - Contamination by  carry-over  can occur whenever high level and low level sam- ples are sequentially analyzed. To reduce carry-over, the purging device and sample syringe must be rinsed with reagent water between sample analyses. Whenever an un- usually concentrated sample  is  encountered, it should be followed by an analysis of rea- gent water to check for cross contamination. For samples containing large amounts of water-soluble materials, suspended solids, high boiling compounds or high aromatic levels, it may be necessary to wash the purg- ing device with a detergent solution, rinse it with distilled water, and then dry it in an oven at 105 C between analyses. The  trap and other parts of the system are  also  sub- ject to contamination; therefore, frequent bakeout and purging of the entire system may be required.

- Safety

  - The toxicity or carcinogenicity of each reagent used in this method has not been precisely defined; however, each chem- ical compound should be treated as a poten- tial health hazard. From this viewpoint, ex- posure to these chemicals must be reduced to the lowest possible level by whatever means available. The laboratory is responsible for maintaining a current awareness file of OSHA regulations regarding the safe han- dling of the chemicals specified in this meth- od. A reference file of material data handling sheets should also be made available to all personnel involved in the chemical analysis. Additional  references  to  laboratory  safety

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 602

are available and have been identified 4 6 for the information of the analyst.

  - The following parameters covered by this method have been  tentatively  classified as known or suspected, human or mamma- lian carcinogens: benzene and 1,4- dichlorobenzene. Primary standards of these toxic compounds should be prepared in a hood. A NIOSH/MESA approved toxic gas respirator should be worn when the analyst handles high concentrations of these toxic compounds.

- Apparatus and Materials

  - Sampling equipment, for discrete sam- pling.

    - Vial]25-mL capacity or  larger, equipped with a screw cap with a hole in the center (Pierce #13075 or equivalent). Deter- gent wash, rinse with tap and distilled  water, and dry at 105 C before use.

    - Septum—Teflon-faced	silicone (Pierce #12722 or equivalent). Detergent wash, rinse with tap and distilled water, and dry at 105 C for 1 h before use.

  - Purge and trap system—The purge and trap system consists of three separate pieces of equipment: A purging device, trap, and desorber. Several complete systems are now commercially available.

    - The purging device must be designed to accept 5-mL samples with a water column at least 3 cm deep. The gaseous head space between the water column and the trap must have a total volume of less than 15 mL. The purge gas  must  pass through  the  water col- umn as finely divided bubbles with a diame- ter of less than 3 mm at the origin. The purge gas must be introduced no more than

5 mm from the base of the water  column. The purging device illustrated in Figure 1 meets these design criteria.

    - The trap must be at least 25 cm long and have an inside diameter of at least 0.105 in.

      - The trap is packed with 1 cm of methyl silicone coated  packing  (Section 6.4.2) and 23 cm of 2,6-diphenylene oxide poly- mer (Section 6.4.1) as shown in Figure 2. This trap was used to develop the method per- formance statements in Section 12.

      - Alternatively, either of the two traps described in Method 601 may be used, although water vapor will preclude the meas- urement of low concentrations of benzene.

    - The desorber must be capable of rap- idly heating the trap to 180 C. The polymer section of  the trap  should not  be heated higher than 180 C and the remaining sec- tions should not exceed 200 C. The desorber illustrated in Figure 2 meets these design criteria.

    - The purge and trap system may be assembled as a separate unit or be coupled to a gas chromatograph as illustrated in Fig- ures 3, 4, and 5.

  - Gas chromatograph—An analytical system complete  with  a  temperature  pro- grammable gas chromatograph suitable for on-column injection and all required acces- sories including syringes, analytical  col- umns, gases, detector, and strip-chart re- corder. A data system is recommended for measuring peak areas.

    - Column 1—6 ft long 0.082 in. ID stainless steel or glass, packed with 5% SP– 1200 and 1.75% Bentone-34 on Supelcoport (100/120 mesh) or  equivalent.  This  column was used to develop the method performance statements in Section 12. Guidelines for the use of alternate column packings  are  pro- vided in Section 10.1.

    - Column 2—8 ft long 0.1 in ID stain- less steel or glass, packed with 5% 1,2,3- Tris(2-cyanoethoxy)propane on Chromosorb W-AW (60/80 mesh) or equivalent.

    - Detector—Photoionization detector (h-Nu Systems, Inc. Model PI–51–02 or equiv- alent). This type of detector has been proven effective in the analysis of wastewaters  for the parameters listed in the scope (Section 1.1), and was used to develop the method per- formance statements in Section 12. Guide- lines for the use of alternate detectors are provided in Section 10.1.

  - Syringes—5-mL glass hypodermic with Luerlok tip (two each), if applicable to the purging device.

  - Micro syringes—25-L, 0.006 in. ID nee- dle.

  - Syringe valve—2-way, with Luer ends (three each).

  - Bottle—15-mL, screw-cap, with Teflon cap liner.

  - Balance—Analytical, capable of accu- rately weighing 0.0001 g.

- Reagents

  - Reagent water—Reagent water is de- fined as a water in which an  interferent  is not observed at the  MDL  of  the  parameters of  interest.

    - Reagent water can be generated by passing tap water through a carbon filter bed containing about 1 lb of activated carbon (Filtrasorb-300, Calgon Corp., or equivalent).

    - A water  purification  system (Millipore Super-Q or equivalent)  may  be used to generate reagent water.

    - Reagent water may also be prepared by boiling water for 15 min. Subsequently, while maintaining the temperature at 90 C, bubble a contaminant-free inert gas through the water for 1 h. While  still  hot,  transfer the water to a narrow mouth screw-cap bot- tle and  seal with  a  Teflon-lined septum  and cap.

  - Sodium thiosulfate—(ACS) Granular.

  - Hydrochloric acid (1 +  1)—Add  50  mL of concentrated HCl (ACS) to 50 mL of rea- gent  water.

  - Trap Materials:

#### Pt. 136, App. A, Meth. 602

    - 2,6-Diphenylene oxide polymer— Tenax, (60/80 mesh), chromatographic  grade or   equivalent.

    - Methyl silicone packing—3% OV–1 on Chromosorb-W (60/80 mesh) or equivalent.

  - Methanol—Pesticide quality or equiv- alent.

  - Stock standard solutions—Stock standard solutions may be prepared from pure standard materials or purchased as cer- tified solutions. Prepare stock standard solu- tions in methanol using assayed liquids. Be- cause of the toxicity of benzene and 1,4- dichlorobenzene, primary dilutions of these materials should be prepared in a hood. A NIOSH/MESA approved toxic gas respirator should be used when the analyst handles high concentrations of such materials.

    - Place about  9.8  mL  of  methanol  into a 10–mL ground glass stoppered volumetric flask. Allow the flask to stand,  unstoppered, for about 10 min or until all alcohol wetted surfaces have dried. Weigh the flask to the nearest 0.1 mg.

    - Using a 100–L syringe, immediately

add two or more drops of assayed reference material to the flask, then reweigh. Be sure that the drops fall directly into the alcohol without contacting the neck of the flask.

    - Reweigh, dilute to volume, stopper, then mix by inverting the flask  several times. Calculate the concentration in g/L from the net gain in weight. When compound purity is assayed to be 96% or greater, the weight can be used without correction to cal- culate the concentration of the stock stand- ard. Commercially prepared stock standards can be used at any concentration if they are certified by the manufacturer or by an inde- pendent source.

    - Transfer the stock standard solution into a Teflon-sealed screw-cap  bottle.  Store at 4 C and protect from light.

    - All standards must be replaced after one month, or sooner if comparison with check standards indicates a problem.

  - Secondary dilution standards—Using stock standard solutions, prepare secondary dilution standards in methanol that contain the compounds of interest, either singly or mixed together. The secondary dilution standards should be prepared at concentra- tions such that the aqueous calibration standards prepared in Section 7.3.1 or 7.4.1 will bracket the working range of the ana- lytical system. Secondary solution standards must be stored with zero headspace and should be checked frequently for signs of degradation or evaporation, especially just prior to preparing calibration standards from them.

  - Quality control check sample con- centrate—See Section 8.2.1.

- Calibration

  - Assemble a purge and trap system that meets the specifications in Section 5.2. Con-

#### 40 CFR Ch. I (7–1–17 Edition)

dition the trap overnight at 180 C by backflushing with an inert gas flow of at least 20 mL/min. Condition the trap for 10 min once daily prior to use.

  - Connect the purge and trap system to a gas chromatograph. The gas chro- matograph must be operated using tempera- ture and flow rate conditions equivalent to those given in Table 1. Calibrate the purge and trap-gas chromatographic system using either the external standard technique (Sec- tion 7.3) or the internal standard technique (Section 7.4).

  - External standard calibration proce- dure:

    - Prepare calibration standards at a minimum of three concentration levels for each parameter by carefully adding 20.0 L of one or more secondary dilution standards to 100, 500, or 1000 mL of reagent water. A 25-L syringe with a 0.006 in. ID needle should be used for this operation. One of the external standards should be at a concentration near, but above, the MDL (Table 1) and the other concentrations should correspond to the ex- pected range of concentrations found in real samples or should define the working range of the detector. These aqueous  standards must be prepared fresh daily.

    - Analyze each calibration standard according to Section 10, and tabulate peak height or area responses versus the con- centration in the standard. The results can be used to prepare a calibration curve for each compound. Alternatively, if the ratio of response to concentration (calibration fac- tor) is a constant over the working range (<10% relative standard deviation, RSD), lin- earity through the origin can be assumed and the average ratio or calibration factor can be used in place of a calibration curve.

  - Internal standard calibration proce- dure—To use this approach, the analyst must select one or more internal standards that are similar in analytical behavior to the compounds of interest. The analyst must fur- ther demonstrate that the measurement of the internal standard is not affected by method or matrix interferences. Because of these limitations, no internal standard  can be suggested that is applicable to all sam- ples. The compound, a,a,a,-trifluorotoluene, recommended as a surrogate spiking com- pound in Section 8.7 has been used success- fully as an internal standard.

    - Prepare calibration standards at a minimum of three concentration levels  for each parameter of interest as described in Section 7.3.1.

    - Prepare a spiking solution con- taining each of the internal standards  using the procedures described in Sections 6.6 and

6.7. It is recommended that the secondary di- lution standard be prepared at a concentra- tion of 15 g/mL of each internal standard compound.   The   addition   of   10   l   of   this

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 602

standard to 5.0 mL of sample or calibration standard would be equivalent to 30 g/L.

    - Analyze each calibration standard according to Section 10, adding 10 L of in- ternal  standard  spiking  solution  directly  to the syringe  (Section  10.4).  Tabulate  peak height or  area  responses against  concentra- tion for each compound and internal stand- ard, and calculate response factors (RF) for each  compound  using  Equation  1.

RF = (As)(Cis (Ais)(Cs)

Equation  1 where:

As  = Response for the parameter to be meas-

ured.

Ais = Response for the internal standard.

Cis  = Concentration of the internal standard Cs  = Concentration of the parameter to be

measured.

If the RF value over the working range is a constant (<10% RSD), the RF can be assumed to be invariant and the average RF can be used for calculations. Alternatively, the re- sults can be used to plot a calibration curve of response ratios, As/Ais, vs. RF.

  - The working calibration curve, cali- bration factor, or RF must be verified on each working day by the measurement  of  a QC check sample.

    - Prepare the QC check sample as de- scribed in Section 8.2.2.

    - Analyze the QC check sample accord- ing to Section 10.

    - For each parameter, compare the re- sponse (Q) with the corresponding calibra- tion acceptance criteria found in Table 2. If the responses for all parameters of interest fall within the designated ranges, analysis of actual samples can begin. If any individual Q falls outside the range, a new calibration curve, calibration factor, or RF must be pre- pared for that parameter according to Sec- tion 7.3 or 7.4.

- Quality Control

  - Each laboratory that uses this method is required to operate a formal quality con- trol program. The  mimimum requirements of this program consist of an initial dem- onstration of laboratory capability and an ongoing analysis of spiked samples to evalu- ate and document data quality. The labora- tory must maintain records to document the quality of data that is generated. Ongoing data quality checks are compared with es- tablished performance criteria to determine if the results of analyses meet the perform- ance characteristics of the method. When re- sults of sample spikes indicate atypical method performance, a quality control check standard must be analyzed to confirm that the measurements were performed in an in- control mode of operation.

    - The analyst must make an initial, one-time, demonstration of the ability to generate acceptable accuracy and precision

with this method. This  ability  is  established as described in Section 8.2.

    - In recognition of advances that are occurring in chromatography, the analyst is permitted certain  options  (detailed  in  Sec- tion 10.1) to improve the separations or lower the cost of measurements. Each time such a modification is made to the method, the ana- lyst is required to repeat the procedure in Section 8.2.

    - Each day, the analyst must analyze a reagent water blank to demonstrate that interferences from the analytical system are under control.

    - The laboratory must, on an ongoing basis, spike and analyze a minimum of 10% of all samples to monitor and evaluate lab- oratory data quality. This procedure is de- scribed in Section 8.3.

    - The laboratory must, on an ongoing basis, demonstrate through the analyses of quality control  check standards  that  the op- eration of the measurement system is in con- trol.  This  procedure  is  described  in  Section

8.4. The frequency of the check standard analyses is equivalent to 10% of all samples analyzed but may be reduced if spike recov- eries from samples (Section 8.3) meet all specified quality control criteria.

    - The laboratory must maintain per- formance records to document the quality of data that is generated. This procedure is de- scribed in Section 8.5.

  - To establish the ability to generate acceptable accuracy and precision, the ana- lyst must perform the following operations.

    - A quality control (QC) check sample concentrate is required containing each pa- rameter of  interest  at a  concentration  of  10

g/mL in methanol. The QC check sample concentrate must be obtained from the U.S. Environmental Protection Agency, Environ- mental Monitoring and Support Laboratory in Cincinnati, Ohio, if available. If not avail- able from that source, the QC check sample concentrate must be obtained from another external source. If not available from either source above, the QC check sample con- centrate must be prepared by the laboratory using stock standards prepared independ- ently from those used for calibration.

    - Prepare a QC check sample to con- tain 20 g/L of each parameter by adding 200

L of QC check sample concentrate to 100 mL of reagant water.

    - Analyze four 5-mL aliquots of the well-mixed QC check sample according to Section 10.

    - Calculate the average recovery (X¯ ) in

g/L, and the standard deviation of the re- covery (s) in g/L, for each parameter of in- terest using the four results.

    - For each parameter compare s and X¯

with the corresponding acceptance criteria for   precision   and   accuracy,   respectively,

#### Pt. 136, App. A, Meth. 602

found in Table 2. If s and X¯ for all param- eters of interest meet the acceptance cri- teria, the system performance is acceptable and analysis of actual samples can begin. If

any individual s exceeds the precision limit or any individual X¯  falls outside the range

for accuracy, the system performance is un- acceptable for that parameter.

NOTE: The large number of parameters in Table 2 present  a  substantial  probability that one or more will fail at least one of the acceptance criteria when all parameters are analyzed.

    - When one or more of the parameters tested fail at least one of the acceptance cri- teria, the analyst must proceed according to Section 8.2.6.1 or 8.2.6.2.

      - Locate and correct the source of the problem and repeat the test for all pa- rameters of interest beginning with Section 8.2.3.

      - Beginning with Section 8.2.3, repeat the test only for those  parameters  that failed to meet criteria. Repeated failure, however, will confirm a  general  problem with the measurement system. If this occurs, locate and correct the source of the problem and repeat the test for all compounds of in- terest beginning with Section 8.2.3.

  - The laboratory must, on an ongoing basis, spike at least 10% of the samples from each sample site being monitored to assess accuracy. For laboratories analyzing one to ten samples per month, at least one spiked sample per month is required.

    - The concentration of the spike in the sample should be determined as follows:

      - If, as in compliance monitoring, the concentration of a specific parameter in the sample is being checked against a regu- latory concentration limit, the spike should be at that limit or 1 to 5 times higher than the background concentration determined in Section 8.3.2, whichever concentration would be larger.

      - If the concentration of a specific parameter in the sample  is  not  being checked against a limit specific to that pa- rameter, the spike should be at 20 g/L or 1 to 5  times  higher than  the  background  con- centration determined in Section 8.3.2, whichever concentration would be larger.

    - Analyze one 5-mL sample aliquot to determine the background concentration (B) of each parameter. If necessary, prepare a new QC check sample concentrate (Section 8.2.1) appropriate for the background con- centrations in the sample. Spike a second 5- mL sample aliquot with 10 L of the QC check sample concentrate and analyze it to determine   the   concentration   after   spiking

(A) of each parameter. Calculate each per- cent recovery (P) as 100(A¥B)%/T, where T is the known true value of the spike.

    - Compare the percent recovery (P) for each parameter with the corresponding QC acceptance  criteria  found  in  Table  2.  These

#### 40 CFR Ch. I (7–1–17 Edition)

acceptance criteria were calculated to  in- clude an allowance for  error  in  measurement of both the background and spike concentra- tions, assuming a spike  to  background  ratio of 5:1. This error will be accounted for to the extent that  the  analyst’s  spike  to  back- ground ratio approaches 5:1. 7 If spiking was performed  at  a  concentration  lower  than  20

g/L, the analyst must use either the QC ac- ceptance criteria in Table 2, or optional QC acceptance criteria calculated  for the  spe- cific spike concentration. To calculate op- tional acceptance criteria for the recovery of a parameter: (1) Calculate accuracy (X) using the equation in Table 3,  substituting the spike concentration (T) for C; (2) cal- culate  overall  precision  (S)  using  the  equa-

tion in Table 3, substituting Xfor X¯ ; (3) cal-

culate the range for recovery at the spike concentration as (100 X/T) 2.44(100 S/T)%. 7

    - If any individual P falls outside the designated range for recovery, that param- eter has failed the acceptance criteria. A check standard containing each parameter that failed the criteria must be analyzed as described in Section 8.4.

  - If any parameter fails the acceptance criteria for recovery in Section 8.3, a QC check standard containing each parameter that failed must be prepared and analyzed.

NOTE: The frequency for the required anal- ysis of a QC check standard will depend upon the number of parameters being simulta- neously tested, the complexity of the sample matrix, and the performance of the labora- tory.

    - Prepare the QC check standard by adding 10 L of QC check sample concentrate (Section 8.2.1 or 8.3.2) to 5 mL of reagent water. The QC check standard needs only to contain  the  parameters  that   failed   criteria in the  test in  Section 8.3.

    - Analyze the QC check standard to determine the concentration measured (A) of each parameter. Calculate each percent re- covery (Ps) as 100 (A/T)%, where T is the true value of the standard concentration.

    - Compare the percent recovery (Ps) for each parameter with the corresponding QC acceptance criteria found in Table 2. Only parameters that failed the test in Section 8.3 need to be compared with these  criteria.  If the recovery of any such parameter falls out- side the designated range, the laboratory performance for that parameter is judged to be out of control, and the problem must be immediately identified and corrected. The analytical result for that parameter in the unspiked sample is suspect  and may not  be reported for regulatory compliance purposes.

  - As part of the QC program for the lab- oratory, method accuracy for wastewater samples must be assessed and records must be maintained. After the analysis of five spiked wastewater samples as in Section 8.3,

calculate  the  average  percent  recovery  (P¯ )

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 602

and the standard deviation of the percent re- covery (sp). Express the accuracy assessment as a percent recovery interval from P¯ ¥2sp  to

P¯ + 2sp. If P¯ = 90% and sp = 10%, for example,

the accuracy interval is expressed as 70– 110%. Update the accuracy  assessment  for each parameter on a regular basis (e.g. after each five to  ten  new  accuracy  measure- ments).

  - It is recommended that the laboratory adopt additional quality assurance practices for use  with  this method.  The  specific  prac- tices that  are  most  productive  depend  upon the needs of the laboratory and the nature of the samples. Field duplicates may be ana- lyzed to assess the precision of the environ- mental measurements. When doubt exists over the identification of a peak on the chro- matogram, confirmatory techniques such as gas chromatography with a dissimilar col- umn, specific element detector, or mass spectrometer must be used. Whenever pos- sible, the laboratory should analyze standard reference materials and participate in rel- evant performance evaluation studies.

  - The analyst should monitor both the performance  of  the  analytical  system  and the effectiveness of the method in dealing with each sample matrix by spiking each sample, standard, and reagent water blank with surrogate compounds (e.g. a, a, a,- trifluorotoluene) that encompass the  range of the temperature program used in this method. From stock standard solutions pre- pared as in Section 6.6, add a volume to give 750 g of each surrogate to 45 mL of reagent water contained in a 50-mL volumetric flask, mix and dilute to volume for a concentration of 15 mg/L. Add 10 L of this surrogate spik- ing solution directly into the 5-mL syringe with every sample and reference standard analyzed. Prepare a fresh surrogate spiking solution on a weekly basis. If the internal standard calibration procedure is being used, the surrogate compounds may be added di- rectly to the internal standard spiking solu- tion (Section 7.4.2).

- Sample Collection, Preservation, and Handling

  - The samples must be iced or refrig- erated from the time of collection until anal- ysis. If the sample contains free or combined chlorine, add sodium  thiosulfate  preserva- tive (10 mg/40 mL is sufficient for up to  5 ppm Cl2) to the empty sample bottle just prior to shipping to the sampling site. EPA Method 330.4 or 330.5 may be used for meas- urement of residual chlorine. 8 Field test kits are available for this purpose.

  - Collect about 500 mL of sample in a clean container. Adjust the pH of the sample to about 2 by adding 1 + 1 HCl while stirring. Fill the sample bottle in such a manner that no air bubbles pass through the sample as the bottle is being filled. Seal the bottle so that no air bubbles are entrapped in it. Main-

tain the hermetic seal on the sample bottle until time of analysis.

  - All samples must be analyzed  within 14 days of collection. 3

- Procedure

10.1 Table 1 summarizes the recommended operating conditions for the gas chro- matograph. Included in this table are esti- mated retention times and MDL that can be achieved under these conditions. An example of the separations achieved by Column 1 is shown in Figure 6. Other packed columns, chromatographic conditions,  or  detectors may  be  used  if  the  requirements  of  Section

8.2 are met.

  - Calibrate the system daily as de- scribed in Section 7.

  - Adjust the purge gas (nitrogen or he- lium) flow rate to 40 mL/min. Attach the trap inlet to the purging device, and set the purge and trap system to purge (Figure 3). Open the syringe valve located on the purg- ing device sample introduction needle.

  - Allow the sample to come to ambient temperature prior to introducing it to the syringe. Remove the plunger from a 5-mL sy- ringe and attach a closed syringe valve. Open the sample bottle (or standard) and carefully pour the sample into the syringe barrel  to just short of overflowing. Replace the sy- ringe plunger and compress the sample. Open the syringe valve and vent any residual air while adjusting the sample volume to 5.0 mL. Since this process of taking an aliquot de- stroys the validity of the sample for future analysis, the analyst should fill a second sy- ringe at this time to protect against possible loss of data. Add 10.0 L of the surrogate spiking solution (Section 8.7) and 10.0 L of the internal standard spiking solution (Sec- tion 7.4.2), if applicable, through the valve bore, then close the valve.

  - Attach the syringe-syringe valve as- sembly to the syringe valve on the purging device. Open the syringe valves and  inject the sample into the purging chamber.

  - Close both valves and purge the sam- ple for 12.0 0.1 min at ambient temperature.

  - After the 12-min purge time, dis- connect the purging device from the trap. Dry the trap by maintaining a flow of 40 mL/ min of dry purge gas through it for 6 min (Figure 4). If the purging device has no provi- sion for bypassing the purger for this step, a dry purger should be inserted into the device to minimize moisture in the gas. Attach the trap to the chromatograph, adjust the purge and trap system to the desorb mode (Figure 5), and begin to temperature program the gas chromatograph. Introduce the trapped mate- rials to the GC column by  rapidly  heating the trap to 180 C while backflushing the trap with an inert gas between 20 and 60 mL/min for 4 min. If rapid heating of the trap cannot be achieved, the GC column must be used as

#### Pt. 136, App. A, Meth. 602

a secondary trap by cooling it to 30 C (sub- ambient temperature, if poor peak geometry and random retention time problems persist) instead of the initial program temperature of 50 C.

  - While the trap is being desorbed into the gas chromatograph column, empty the purging chamber using the sample introduc- tion syringe. Wash the chamber with two 5- mL flushes of reagent water.

  - After desorbing the sample for 4 min, recondition the trap by returning the purge and trap system to the purge mode. Wait 15 s, then close the syringe valve  on  the  purg- ing device to begin gas flow through the trap. The trap temperature should be main- tained at 180 C. After approximately 7 min, turn off the trap heater and open the syringe valve to stop  the gas  flow through  the trap. When the trap is cool,  the  next  sample  can be analyzed.

  - Identify the parameters in the sam- ple by comparing the retention times of the peaks in the sample chromatogram with those of the peaks in standard chromatograms. The width of the retention time window used to make identifications should be based upon measurements of ac- tual retention time variations of standards over the course of a day. Three times the standard deviation of a retention time for a compound can be used to calculate a sug- gested window size; however, the experience of the analyst should weigh heavily in the interpretation of chromatograms.

  - If the  response  for a  peak  exceeds the working range of the system, prepare a dilution of the sample with reagent water from the aliquot in the second syringe and reanalyze.

- Calculations

  - Determine the concentration of indi- vidual compounds in the sample.

    - If the external standard calibration procedure is used, calculate the concentra- tion of the parameter being measured from the peak response using the calibration curve or calibration factor determined in Section 7.3.2.

    - If the internal standard calibration procedure is used, calculate the concentra- tion in the sample using the response factor (RF) determined in Section 7.4.3 and Equa- tion 2.

As Cis 

## Concentration (g/L) 

Ais RF

Equation  2 where:

As  = Response for the parameter to be meas- ured.

Ais = Response for the internal standard.

Cis = Concentration of the internal standard.

#### 40 CFR Ch. I (7–1–17 Edition)

  - Report results in g/L without correc- tion for recovery data. All QC data obtained should be reported with the sample results.

- Method Performance

  - The method detection limit (MDL) is defined as the minimum concentration of a substance that can be measured and reported with 99% confidence that the value is above zero. 1 The MDL concentrations listed  in Table 1 were obtained using reagent water. 9 Similar results were achieved using rep- resentative wastewaters. The MDL actually achieved in a given analysis will vary de- pending on instrument sensitivity and ma- trix  effects.

  - This method has been  demonstrated to be applicable for the concentration range from the MDL to 100 MDL. 9 Direct aqueous injection techniques should be used to meas- ure concentration levels above 1000 MDL.

  - This method was tested by 20 labora- tories using reagent water, drinking water, surface water, and three industrial wastewaters spiked at six concentrations over the range 2.1 to 550 g/L. 9 Single oper- ator precision, overall precision, and method accuracy were found to be directly related to the concentration of the parameter and es- sentially independent of the sample matrix. Linear equations to describe these relation- ships are presented in Table 3.

References

- 40 CFR part 136, appendix B.

- Lichtenberg, J.J. ‘‘Determining Volatile Organics  at  Microgram-per-Litre-Levels  by Gas  Chromatography,’’  Journal   American Water Works Association, 66, 739 (1974).

- Bellar, T.A., and Lichtenberg, J.J. ‘‘Semi-Automated Headspace Analysis of Drinking Waters and Industrial Waters for Purgeable Volatile Organic Compounds,’’ Proceedings of Symposium on Measurement of Organic Pollutants in Water and Waste- water. American Society for Testing and Ma- terials, STP 686, C.E. Van Hall, editor, 1978.

- ‘‘Carcinogens—Working with Carcino- gens,’’ Department of Health, Education, and Welfare, Public Health Service, Center for Disease Control, National Institute for Occu- pational Safety and Health. Publication No. 77–206, August 1977.

- ‘‘OSHA Safety and Health Standards, General Industry,’’ (29 CFR part 1910), Occu- pational Safety and Health Administration, OSHA 2206 (Revised, January 1976).

- ‘‘Safety in Academic Chemistry Labora- tories,’’ American Chemical Society Publica- tion, Committee on Safety, 3rd Edition, 1979.

- Provost,  L.P.,  and  Elder,  R.S.  ‘‘Interpre- tation   of   Percent   Recovery   Data,’’   American Laboratory, 15, 58-63  (1983).  (The  value  2.44 used  in  the  equation  in  Section  8.3.3.  is  two times the value 1.22 derived in this report.)

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 602

8.‘‘Methods 330.4 (Titrimetric, DPD-FAS) and 330.5 (Spectrophotometric, DPD) for Chlorine, Total Residual,’’ Methods for Chemical Analysis of Water and Wastes, EPA–600/4–79–020, U.S. Environmental Pro- tection Agency, Office of Research and De- velopment, Environmental Monitoring and Support Laboratory, Cincinnati, Ohio 45268. March 1979.

9. ‘‘EPA Method Study 25, Method 602, Purgeable Aromatics,’’ EPA 600/4–84–042, Na- tional Technical Information Service, PB84– 196682, Springfield, Virginia 22161, May 1984.

TABLE 1—CHROMATOGRAPHIC CONDITIONS AND

| Parameter | Retention time (min) | Method detection limit (g/ L) |
| --- | --- | --- |
|  | Column 1 | Column 2 |  |
| Benzene ........................ | 3.33 | 2.75 | 0.2 |

METHOD DETECTION LIMITS

TABLE 1—CHROMATOGRAPHIC CONDITIONS AND

METHOD DETECTION LIMITS—Continued

| Parameter | Retention time (min) | Method detection limit (g/ L) |
| --- | --- | --- |
|  | Column 1 | Column 2 |  |
| Toluene .......................... | 5.75 | 4.25 | 0.2 |
| Ethylbenzene ................. | 8.25 | 6.25 | 0.2 |
| Chlorobenzene .............. | 9.17 | 8.02 | 0.2 |
| 1,4-Dichlorobenzene ..... | 16.8 | 16.2 | 0.3 |
| 1,3-Dichlorobenzene ..... | 18.2 | 15.0 | 0.4 |
| 1,2-Dichlorobenzene ..... | 25.9 | 19.4 | 0.4 |

Column 1 conditions: Supelcoport (100/120 mesh) coated with 5% SP–1200/1.75% Bentone-34 packed in a 6 ft 0.085 in. ID stainless steel column with helium carrier gas at 36 mL/ min flow rate. Column temperature held at 50 C for 2 min then programmed at 6 C/min to 90 C for a final hold.

Column 2 conditions: Chromosorb W-AW (60/80 mesh) coated with 5% 1,2,3-Tris(2-cyanoethyoxy)propane packed in a 6 ft 0.085 in. ID stainless steel column with helium carrier gas at 30 mL/min flow rate. Column temperature held at 40

C for 2 min then programmed at 2 C/min to 100 C for a final hold.

TABLE 2—CALIBRATION AND QC ACCEPTANCE CRITERIA—METHOD 602 A

| Parameter | Range for Q (g/L) | Limit for s (g/L) | Range for X¯ (g/L) | Range for P, Ps(%) |
| --- | --- | --- | --- | --- |
| Benzene .......................................................................................................... | 15.4–24.6 | 4.1 | 10.0–27.9 | 39–150 |
| Chlorobenzene ................................................................................................ | 16.1–23.9 | 3.5 | 12.7–25.4 | 55–135 |
| 1,2-Dichlorobenzene ....................................................................................... | 13.6–26.4 | 5.8 | 10.6–27.6 | 37–154 |
| 1,3-Dichlorobenzene ....................................................................................... | 14.5–25.5 | 5.0 | 12.8–25.5 | 50–141 |
| 1,4-Dichlorobenzene ....................................................................................... | 13.9–26.1 | 5.5 | 11.6–25.5 | 42–143 |
| Ethylbenzene ................................................................................................... | 12.6–27.4 | 6.7 | 10.0–28.2 | 32–160 |
| Toluene ........................................................................................................... | 15.5–24.5 | 4.0 | 11.2–27.7 | 46–148 |

Q = Concentration measured in QC check sample, in g/L (Section 7.5.3).

s = Standard deviation of four recovery measurements, in g/L (Section 8.2.4). X¯ = Average recovery for four recovery measurements, in g/L (Section 8.2.4).

Ps, P = Percent recovery measured (Section 8.3.2, Section 8.4.2).

a Criteria were calculated assuming a QC check sample concentration of 20 g/L.

Note: These criteria are based directly upon the method performance data in Table 3. Where necessary, the limits for recovery have been broadened to assure applicability of the limits to concentrations below those used to develop Table 3.

TABLE 3—METHOD ACCURACY AND PRECISION AS FUNCTIONS OF CONCENTRATION—METHOD 602

| Parameter | Accuracy, as recovery, X (g/L) | Single analyst precision, s (g/L) | Overall preci- sion, S(g/L) |
| --- | --- | --- | --- |
| Benzene ............................................................................................................ Chlorobenzene .................................................................................................. 1,2-Dichlorobenzene ......................................................................................... 1,3-Dichlorobenzene ......................................................................................... 1,4-Dichlorobenzene ......................................................................................... Ethylbenzene ..................................................................................................... Toluene .............................................................................................................. | 0.92C + 0.57 0.95C + 0.02 0.93C + 0.52 0.96C¥0.05 0.93C¥0.09 0.94C + 0.31 0.94C + 0.65 | 0.09X¯ + 0.59 0.09X¯ + 0.23 0.17X¯ ¥0.04 0.15X¯ ¥0.10 0.15X¯ + 0.28 0.17X¯ + 0.46 0.09X¯ + 0.48 | 0.21X¯ + 0.56 0.17X¯ + 0.10 0.22X¯ + 0.53 0.19X¯ + 0.09 0.20X¯ + 0.41 0.26X¯ + 0.23 0.18X¯ + 0.71 |

X= Expected recovery for one or more measurements of a sample containing a concentration of C, in g/L.

S= Expected single analyst standard deviation of measurements at an average concentration found of X¯ , in X g/L. S= Expected interlaboratory standard deviation of measurements at an average concentration found of X¯ , in g/L. C = True value for the Concentration, in g/L.

X¯ = Average recovery found for measurements of samples containing a concentration of C, in g/L.

#### Pt. 136, App. A, Meth. 602

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 602

Pt. 136, App. A, Meth. 602

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 602

Pt. 136, App. A, Meth. 603

METHOD 603—ACROLEIN AND ACRYLONITRILE

- Scope and Application

  - This method covers the determination of acrolein and acrylonitrile. The following parameters may be determined by this meth- od:

| Parameter | STORET No. | CAS No. |
| --- | --- | --- |
| Acrolein ........................................... Acrylonitrile ...................................... | 34210 34215 | 107–02–8 107–13–1 |

  - This is a purge and trap gas chromatographic (GC)  method  applicable  to the determination of the compounds listed above in municipal and  industrial  discharges as provided under 40 CFR 136.1. When this method is  used  to  analyze  unfamiliar  sam- ples for either or both of  the  compounds above, compound identifications should be supported by at least one  additional  quali- tative technique. This method describes ana- lytical conditions for a second gas chromatographic column that can be used to confirm measurements made with the  pri- mary column. Method 624 provides gas chro- matograph/mass spectrometer (GC/MS) con- ditions appropriate for the qualitative and quantitative confirmation of results for the parameters listed above, if used  with  the purge and trap conditions described in this method.

  - The method detection limit (MDL, de- fined in Section 12.1) 1 for each parameter is listed in Table 1. The MDL for a specific wastewater may differ from those listed, de- pending upon the nature of interferences  in the sample matrix.

  - Any modification of this method,  be- yond those expressly permitted, shall be con- sidered as a major modification subject to application and approval of alternate test procedures under 40 CFR 136.4 and 136.5.

  - This method is restricted to use by or under the supervision of analysts experi- enced in the operation of a purge and trap system and a gas chromatograph and in the interpretation of gas chromatograms. Each analyst must demonstrate the ability to gen- erate acceptable results with this method using the procedure described in Section 8.2.

- Summary of Method

  - An inert gas is bubbled through a 5-mL water sample contained in a heated purging chamber. Acrolein and acrylonitrile are transferred from the aqueous phase to the vapor phase. The vapor is swept through a sorbent trap where the analytes are trapped. After the purge is completed, the trap is heated and backflushed with the inert gas to desorb the compound onto a gas chromatographic column. The gas chro- matograph  is  temperature  programmed  to

#### 40 CFR Ch. I (7–1–17 Edition)

separate  the  analytes  which  are  then  de- tected with a flame ionization detector. 2 3

  - The method provides an optional gas chromatographic column that may be help- ful in resolving the compounds of interest from the interferences that may occur.

- Interferences

  - Impurities in the purge gas and or- ganic compound outgassing from the plumb- ing of the trap account for the majority of contamination problems. The analytical sys- tem must be demonstrated to be free from contamination under the conditions of the analysis by running laboratory reagent blanks as described in Section 8.1.3. The use of non-Teflon plastic tubing, non-Teflon thread sealants, or flow controllers with rub- ber components in the purge and trap system should be avoided.

  - Samples can be contaminated by diffu- sion of volatile organics through the septum seal into the sample during shipment and storage. A field reagent blank prepared from reagent water and carried through the sam- pling and handling protocol can serve as a check on such contamination.

  - Contamination by  carry-over  can occur whenever high level and low level sam- ples are sequentially analyzed. To reduce carry-over, the purging device and sample syringe must be rinsed between samples with reagent water. Whenever an unusually con- centrated sample is encountered, it should be followed by an analysis of reagent water to check for cross contamination. For samples containing large amounts of water-soluble materials, suspended solids, high boiling compounds or high analyte levels, it may be necessary to wash the purging device with a detergent solution, rinse it with distilled water, and then dry it in an oven at 105 C between analyses. The trap  and  other  parts of the system are also subject to contamina- tion, therefore, frequent bakeout and purg- ing of the entire system may be required.

- Safety

4.1 The toxicity or  carcinogenicity  of each reagent used in this method has not been precisely defined; however, each chem- ical compound should be treated as a poten- tial health hazard. From this view point, ex- posure to these chemicals must be reduced to the lowest possible level by whatever means available. The laboratory is responsible for maintaining a current awareness file of OSHA regulations regarding the safe han- dling of the chemicals specified in this meth- od. A reference file of material data handling sheets should also be made available to all personnel involved in the chemical analysis. Additional references to laboratory safety are available and have been identified 4 6 for the information of the analyst.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 603

- Apparatus and Materials

  - Sampling equipment, for discrete sam- pling.

    - Vial—25-mL capacity or larger, equipped with a screw cap with a hole in the center (Pierce #13075 or equivalent). Deter- gent wash, rinse with tap and distilled  water, and dry at 105 C before use.

    - Septum—Teflon-faced	silicone (Pierce #12722 or equivalent). Detergent wash, rinse with tap and distilled water and dry at 105 C for 1 h before use.

5.2 Purge and trap system—The purge and trap system consists of three separate pieces of equipment: a purging device, trap, and desorber. Several complete systems are now commercially available.

5.2.1 The purging device must be designed to accept 5-mL, samples with a water column at least 3 cm deep. The gaseous head space between the water column and the trap must have a total volume of less than 15 mL. The purge gas  must pass  through  the water  col- umn as finely divided bubbles with a diame- ter of less than 3 mm at the origin. The purge gas must be introduced no more than

5 mm from the base of the water  column. The purging device must be capable of being heated to 85 C within 3.0 min after transfer of the sample to  the  purging  device  and being held at 85 2 C during the purge cycle. The entire water column in the purging de- vice must be heated. Design of this modifica- tion to the standard purging device is op- tional, however, use of a water bath is sug- gested.

      - Heating mantle—To be used to heat water bath.

      - Temperature controller—Equipped with thermocouple/sensor to accurately con- trol water bath temperature to 2 C. The purging device  illustrated  in Figure  1  meets these design criteria.

    - The trap must be at least 25 cm long and have an inside diameter of at least 0.105 in. The trap must be packed  to  contain  1.0 cm of methyl silicone coated packing (Sec- tion 6.5.2) and 23 cm of 2,6-diphenylene oxide polymer (Section 6.5.1). The minimum speci- fications for the trap are illustrated in  Fig- ure 2.

    - The desorber must be capable of rap- idly heating the trap to 180 C, The desorber illustrated in Figure 2 meets these design criteria.

    - The purge and trap system may be assembled as a separate unit as illustrated in Figure 3 or be coupled to a gas chro- matograph.

  - pH paper—Narrow pH range, about 3.5 to 5.5 (Fisher Scientific Short Range Alkacid No. 2, #14–837–2 or equivalent).

  - Gas chromatograph—An analytical system complete  with  a  temperature  pro- grammable gas chromatograph suitable for on-column  injection  and  all  required  acces-

sories including syringes, analytical col- umns, gases, detector, and strip-chart re- corder. A data system is recommended for measuring peak areas.

    - Column 1—10 ft long 2 mm ID glass or stainless steel, packed with Porapak-QS (80/100 mesh) or equivalent. This column was used to develop the method performance statements in Section 12. Guidelines for the use of alternate column packings  are  pro- vided in Section 10.1.

    - Column 2—6 ft long 0.1 in. ID glass or stainless  steel,  packed  with  Chromosorb 101 (60/80 mesh) or equivalent.

    - Detector—Flame ionization detector. This type of detector has proven effective in the analysis of wastewaters for the param- eters listed in the scope (Section 1.1), and was used to develop the method performance statements in Section 12. Guidelines for the use of alternate detectors are provided in Section 10.1.

  - Syringes—5-mL,  glass  hypodermic with Luerlok tip (two each).

  - Micro syringes—25-L, 0.006 in. ID nee- dle.

  - Syringe valve—2-way, with Luer ends (three each).

  - Bottle—15-mL, screw-cap, with Teflon cap liner.

  - Balance—Analytical, capable of accu- rately weighing 0.0001 g.

- Reagents

  - Reagent water—Reagent water is de- fined as a water in which  an  interferent  is not observed at the  MDL  of  the  parameters of  interest.

    - Reagent water can be generated by passing tap water through a carbon filter bed containing about 1 lb of activated carbon (Filtrasorb-300, Calgon Corp., or equivalent).

    - A water  purification  system (Millipore Super-Q or equivalent)  may  be used to generate reagent water.

    - Regent water may also be  prepared by boiling water for 15 min. Subsequently, while maintaining the temperature at 90 C, bubble a contaminant-free inert gas through the water for 1 h. While  still  hot,  transfer the water to a narrow mouth screw-cap bot- tle and  seal with  a  Teflon-lined septum  and cap.

  - Sodium thiosulfate—(ACS) Granular.

  - Sodium hydroxide solution (10 N)— Dissolve 40 g of NaOH (ACS) in reagent water and dilute to 100 mL.

  - Hydrochloric acid (1 + 1)—Slowly,  add 50 mL of concentrated HCl (ACS) to 50 mL of reagent   water.

  - Trap Materials:

    - 2,6-Diphenylene oxide  polymer— Tenax (60/80 mesh), chromatographic  grade or   equivalent.

    - Methyl silicone packing—3% OV–1 on Chromosorb-W (60/80 mesh) or equivalent.

#### Pt. 136, App. A, Meth. 603

  - Stock standard solutions—Stock standard solutions may be prepared from pure standard materials or purchased as cer- tified solutions. Prepare stock standard solu- tions in reagent water using assayed liquids. Since acrolein and acrylonitrile are lachrymators, primary dilutions of these compounds should be prepared in a hood. A NIOSH/MESA approved toxic gas respirator should be used when the analyst handles high concentrations of such materials.

    - Place about 9.8 mL of reagent water into a 10-mL ground glass stoppered  volu- metric flask. For acrolein standards the rea- gent water must be adjusted to pH 4 to 5. Weight the flask to the nearest 0.1 mg.

    - Using a 100-L  syringe, immediately

add two or more drops of assayed reference material to the flask, then reweigh. Be sure that the drops fall directly into the water without contacting the neck of the flask.

    - Reweigh, dilute to volume, stopper, then mix by inverting the flask  several times. Calculate the concentration in g/L from the net gain in weight. When compound purity is assayed to be 96% or greater, the weight can be used without correction to cal- culate the concentration of the stock staldard. Optionally, stock standard solu- tions may be prepared using the pure stand- ard material by volumetrically measuring the appropriate amounts and determining the weight of the material using the density of the material. Commercially prepared stock standards may be used at any con- centration if they are certified by the manufactaurer or by an independent source.

    - Transfer the stock standard solution into a Teflon-sealed screw-cap  bottle.  Store at 4 C and protect from light.

    - Prepare fresh standards daily.

  - Secondary dilution standards—Using stock standard solutions, prepare secondary dilution standards in reagent water that con- tain the compounds of  interest,  either  singly or mixed together. The secondary dilution standards should be prepared at concentra- tions such that the aqueous calibration standards prepared in Section 7.3.1 or 7.4.1 will bracket the working range of the ana- lytical system. Secondary dilution standards should  be  prepared  daily  and  stored  at  4  C.

  - Quality control check sample con- centrate—See Section 8.2.1.

- Calibration

  - Assemble a purge and trap system that meets the  specifications in  Section 5.2.  Con- dition the trap overnight at 180 C by backflushing with an inert gas flow of at least 20 mL/min. Condition the trap for 10 min once daily prior to use.

  - Connect the purge and trap system to a gas chromatograph. The gas chro- matograph must be operated using tempera- ture and flow rate conditions equivalent to those given in Table 1. Calibrate the purge

#### 40 CFR Ch. I (7–1–17 Edition)

and trap-gas chromatographic system using either the external standard technique (Sec- tion 7.3) or the internal standard technique (Section 7.4).

  - External standard calibration proce- dure:

    - Prepare calibration standards at a minimum of three concentration levels for each parameter by carefully adding 20.0 L of one or more secondary dilution standards to 100, 500, or 1000 mL of reagent water. A 25-L syringe with a 0.006 in. ID needle should be used for this operation. One of the external standards should be at a concentration near, but above, the MDL and the other concentra- tions should correspond to the expected range of concentrations found in real sam- ples or should define the working  range  of the detector. These standards must be pre- pared fresh daily.

    - Analyze each calibration standard according to Section 10, and tabulate peak height or area responses versus the con- centration of the standard. The results can be used to prepare a calibration curve for each compound. Alternatively, if the ratio of response to concentration (calibration fac- tor) is a constant over the working range (<10% relative standard deviation, RSD), lin- earity through the origin can be assumed and the average ratio or calibration factor can be used in place of a calibration curve.

  - Internal standard calibration proce- dure—To use this approach, the analyst must select one or more internal standards that are similar in analytical behavior to the compounds of interest. The analyst must fur- ther demonstrate that the measurement of the internal standard is not affected by method or matrix interferences. Because of these limitations, no internal standard  can be suggested that is applicable to all sam- ples.

    - Prepare calibration standards at a minimum of three concentration levels  for each parameter of interest as described in Section 7.3.1.

    - Prepare a spiking solution con- taining each of the internal standards  using the procedures described in Sections 6.6 and

6.7. It is recommended that the secondary di- lution standard be prepared at a concentra- tion of 15 g/mL of each internal standard compound. The addition of 10 L of this standard to 5.0 mL of sample or calibration standard would be equivalent to 30 g/L.

    - Analyze each calibration standard according to Section 10, adding 10 L of in- ternal  standard  spiking  solution  directly  to the syringe  (Section  10.4).  Tabulate  peak height or  area  responses against  concentra- tion for each compound and internal stand- ard, and calculate response factors (RF) for each  compound  using  Equation  1.

RF = (As)(Cis (Ais)(Cs)

Equation   1

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 603

where:

As  = Response for the parameter to be meas- ured.

Ais = Response for the internal standard.

Cis = Concentration of the internal standard.

Cs  = Concentration of the parameter to be measured.

If the RF value over the working range is a constant (<10% RSD), the RF can be assumed to be invariant and the average RF can be used for calculations. Alternatively, the re- sults can be used to plot a calibration curve of response ratios, As/Ais, vs. RF.

  - The  working  calibration  curve,  cali-

bration factor, or RF must be verified on each working day by the measurement  of  a QC check sample.

    - Prepare the QC check sample as de- scribed in Section 8.2.2.

    - Analyze the QC check sample accord- ing to Section 10.

    - For each parameter, compare the re- sponse (Q) with the corresponding calibra- tion acceptance criteria found in Table 2. If the responses for all parameters of interest fall within the designated ranges, analysis of actual samples can begin. If any individual Q falls outside the range, a new calibration curve, calibration factor, or RF must be pre- pared for that parameter according to Sec- tion 7.3 or 7.4.

- Quality Control

  - Each laboratory that uses this method is required to operate a formal quality  con- trol program. The minimum requirements of this program consist of an initial demonstra- tion of laboratory capability and an ongoing analysis of spiked samples to evaluate and document data quality. The laboratory must maintain records to document the quality of data that is generated. Ongoing data quality checks are compared with established per- formance criteria to determine if the results of analyses meet the performance character- istics of the method. When results of sample spikes indicate atypical method perform- ance, a quality control check  standard  must be analyzed to confirm that the measure- ments were performed in an in-control mode of operation.

    - The analyst must make an initial, one-time, demonstration of the ability to generate acceptable accuracy and precision with this method. This  ability  is  established as described in Section 8.2.

    - In recognition of advances that are occurring in chromatography, the analyst is permitted certain  options  (detailed  in  Sec- tion 10.1) to improve the separations or lower the cost of measurements. Each time such a modification is made to the method, the ana- lyst is required to repeat the procedure in Section 8.2.

    - Each day, the analyst must analyze a reagent  water  blank  to  demonstrate  that

interferences from the analytical system are under control.

    - The laboratory must, on an ongoing basis, spike and analyze a minimum of 10% of all samples to monitor and evaluate lab- oratory data quality. This procedure is de- scribed in Section 8.3.

    - The laboratory must, on an ongoing basis, demonstrate through the analyses of quality control  check standards  that  the op- eration of the measurement system is in con- trol.  This  procedure  is  described  in  Section

8.4. The frequency of the check standard analyses is equivalent to 10% of all samples analyzed but may be reduced if spike recov- eries from samples (Section 8.3) meet all specified quality control criteria.

    - The laboratory must maintain per- formance records to document the quality of data that is generated. This procedure is de- scribed in Section 8.5.

  - To establish the ability to generate acceptable accuracy and precision, the ana- lyst must perform the following operations.

    - A quality control (QC) check sample concentrate is required containing each pa- rameter of  interest  at a  concentration  of  25

g/mL in reagent water. The QC check sam- ple concentrate must be obtained from the

U.S. Environmental Protection Agency, En- vironmental Monitoring and Support Lab- oratory in Cincinnati, Ohio, if available. If not available from that source, the QC check sample concentrate must be obtained from another external source. If not  available from either source above, the QC check sam- ple concentrate must be prepared by the lab- oratory using stock standards prepared inde- pendently from those used for calibration.

    - Prepare a QC check sample to con- tain 50 g/L of each parameter by adding 200

L of QC check sample concentrate to 100 mL of reagent water.

    - Analyze four 5-mL aliquots of the well-mixed QC check sample according to Section 10.

    - Calculate the average recovery (X¯ ) in

g/L, and the standard deviation of the re- covery (s) in g/L, for each parameter using the four results.

    - For each parameter compare s and X¯

with the corresponding acceptance criteria for   precision   and   accuracy,   respectively,

found in Table 3. If s and X¯  for all param-

eters of interest meet the acceptance cri- teria, the system performance is acceptable

and analysis of actual samples can begin. If either s exceeds the precision limit or X¯  falls

outside the range for accuracy, the system performance is unacceptable for that param- eter. Locate and correct the source of the problem and repeat the test for each com- pound of interest.

  - The laboratory must, on an ongoing basis, spike at least 10% of the samples from each sample site being monitored to assess accuracy. For laboratories analyzing one to

#### Pt. 136, App. A, Meth. 603

ten samples per month, at least one spiked sample per month is required.

    - The concentration of the spike in the sample should be determined as follows:

      - If, as in compliance monitoring, the concentration of a specific parameter in the sample is being checked against a regu- latory concentration limit, the spike should be at that limit or 1 to 5 times higher than the background concentration determined in Section 8.3.2, whichever concentration would be larger.

      - If the concentration of a specific parameter in the sample  is  not  being checked against a limit specific to that pa- rameter, the spike should be at 50 g/L or 1 to 5  times  higher than  the  background  con- centration determined in Section 8.3.2, whichever concentration would be larger.

    - Analyze one 5-mL sample aliquot to determine the background concentration (B) of each parameter. If necessary, prepare a new QC check sample concentrate (Section 8.2.1) appropriate for the background con- centrations in the sample. Spike a second 5- mL sample aliquot with 10 L of the QC check sample concentrate and analyze it to determine   the   concentration   after   spiking

(A) of each parameter. Calculate each per- cent recovery (P) as 100(A¥B)%/T, where T is the known true value of the spike.

    - Compare the percent recovery (P) for each parameter with the corresponding QC acceptance criteria found in Table 3. These acceptance criteria were calculated to in- clude an allowance for error in measurement of both the background and spike concentra- tions, assuming a spike  to  background  ratio of 5:1. This error will be accounted for to the extent that the analyst’s spike to back- ground ratio approaches 5:1. 7

    - If any individual P falls outside the designated range for recovery, that param- eter has failed the acceptance criteria. A check standard containing each parameter that failed the criteria must be analyzed as described in Section 8.4.

  - If any parameter fails the acceptance criteria for recovery in Section 8.3, a QC check standard containing each parameter that failed must be prepared and analyzed.

NOTE: The frequency for the required anal- ysis of a QC check standard will depend upon the number of parameters being simulta- neously tested, the complexity of the sample matrix, and the performance of the labora- tory.

    - Prepare the QC check standard by adding 10 L of QC check sample concentrate (Section 8.2.1 or 8.3.2) to 5 mL of reagent water. The QC check standard needs only to contain  the  parameters  that   failed   criteria in the  test in  Section 8.3.

    - Analyze the QC check standard to determine the concentration measured (A) of each parameter. Calculate each percent re-

#### 40 CFR Ch. I (7–1–17 Edition)

covery (Ps) as 100 (A/T)%, where T is the true value of the standard concentration.

    - Compare the percent recovery (Ps) for each parameter with the corresponding QC acceptance criteria found in Table 3. Only parameters that failed the test in Section 8.3 need to be compared with these  criteria.  If the recovery of any such parameter falls out- side the designated range, the laboratory performance for that parameter is judged to be out of control, and the problem must be immediately identified and corrected. The analytical result for that parameter in the unspiked sample is suspect  and may not  be reported for regulatory compliance purposes.

  - As part of the QC program for the lab- oratory, method accuracy for wastewater samples must be assessed and records must be maintained. After the analysis of five spiked wastewater samples as in Section 8.3,

calculate  the  average  percent  recovery  (P¯ )

and the standard deviation of the percent re- covery (sp). Express the accuracy assessment

as a percent recovery interval from P¯ ¥2sp to P¯ + 2sp. If P¯ = 90% and sp = 10%, for example,

the accuracy interval is expressed as 70– 110%. Update the accuracy  assessment  for each parameter on a regular basis (e.g. after each five to  ten  new  accuracy  measure- ments).

  - It is recommended that the laboratory adopt additional quality assurance practices for use  with  this method.  The  specific  prac- tices that  are  most  productive  depend  upon the needs of the laboratory and the nature of the samples. Field duplicates may be ana- lyzed to assess the precision of the environ- mental measurements. When doubt exists over the identification of a peak on the chro- matogram, confirmatory techniques such as gas chromatography with a dissimilar col- umn or mass spectrometer must be used. Whenever possible, the laboratory should analyze standard reference materials and participate in relevant performance evalua- tion  studies.

- Sample Collection, Preservation, and Handling

  - All samples must be iced or refrig- erated from the time of collection until anal- ysis. If the sample contains free or combined chlorine,  add  sodium   thiosulfate   preserva- tive (10 mg/40 mL is sufficient for up to  5 ppm Cl2) to  the  empty  sample  bottle  just prior to shipping to the sampling site. EPA Methods 330.4 and 330.5 may be used for measurement  of   residual   chlorine. 8   Field test  kits  are  available  for  this  purpose.

  - If acrolein is to be analyzed, collect about 500 mL of sample in a clean glass con- tainer. Adjust the pH of the sample to 4 to 5 using acid or base, measuring with narrow range pH paper. Samples for acrolein anal- ysis receiving  no  pH  adjustment  must  be analyzed within 3 days of sampling.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 603

  - Grab samples must be collected in glass containers having a total volume of at least 25 mL. Fill the sample bottle just to overflowing in such a manner that no air bubbles pass through the sample as the bot- tle is being filled. Seal the bottle so that no air bubbles are entrapped in it. If preserva- tive has been added, shake vigorously for 1 min. Maintain the hermetic seal on the sam- ple bottle until time of analysis.

  - All samples must be analyzed  within 14 days of collection. 3

- Procedure

10.1 Table 1 summarizes the recommended operating conditions for the gas chro- matograph. Included in this table are esti- mated retention times and MDL that can be achieved under these conditions. An example of the separations achieved by Column 1 is shown in Figure 5. Other packed columns, chromatographic conditions,  or  detectors may  be  used  if  the  requirements  of  Section

8.2 are met.

  - Calibrate the system daily as de- scribed in Section 7.

  - Adjust the purge gas (nitrogen or he- lium) flow rate to 20 mL-min. Attach the trap inlet to the purging device, and set the purge and trap system to purge (Figure 3). Open the syringe valve located on the purg- ing device sample introduction needle.

  - Remove the plunger from a 5-mL sy- ringe and attach a closed syringe valve. Open the sample bottle (or standard) and carefully pour the sample into the syringe barrel  to just short of overflowing. Replace the sy- ringe plunger and compress the sample. Open the syringe valve and vent any residual air while adjusting the sample volume to 5.0 mL. Since this process of taking an aliquot de- stroys the validity of the sample for future analysis, the analyst should fill a second sy- ringe at this time to protect against possible loss  of  data.  Add  10.0  L  of  the  internal

ringe.   Wash   the   chamber   with   two   5-mL flushes of reagent water.

  - After desorbing the sample  for  1.5 min, recondition the trap by  returning  the purge and trap system to the purge mode. Wait 15 s then close the syringe valve on the purging device to begin gas flow through the trap. The trap temperature should be main- tained at 210 C. After approximately 7 min, turn off the trap heater and open the syringe valve to stop the gas flow through the trap. When the trap is cool,  the  next  sample  can be  analyzed.

  - Identify the parameters in the sam- ple by comparing the retention times of the peaks in the sample chromatogram with those of the peaks in standard chromatograms. The width of the retention time window used to make identifications should be based upon measurements of ac- tual retention time variations of standards over the course of a day. Three times the standard deviation of a retention time for a compound can be used to calculate a sug- gested window size; however, the experience of the analyst should weigh heavily in the interpretation of chromatograms.

- Calculations

  - Determine the concentration of indi- vidual compounds in the sample.

    - If the external standard calibration procedure is used, calculate the concentra- tion of the parameter being measured from the peak response using the calibration curve or calibration factor determined in Section 7.3.2.

    - If the internal standard calibration procedure is used, calculate the concentra- tion in the sample using the response factor (RF) determined in Section 7.4.3 and Equa- tion 2.

As Cis 

## Concentration (g/L) 

standard spiking solution (Section 7.4.2), if applicable, through the valve bore then close the valve.

  - Attach  the  syringe-syringe  valve  as- sembly to the syringe valve on the purging

where:

Ais RF

Equation   2

device.  Open  the  syringe  valves  and  inject the sample into the purging chamber.

  - Close both valves and purge the  sam- ple for 15.0 0.1 min while heating at 85 2 C.

  - After the 15-min purge time, attach the trap to the chromatograph, adjust the purge and trap system to the desorb mode (Figure 4), and begin to temperature pro- gram the gas chromatograph. Introduce the trapped materials to the GC column by rap- idly heating the trap to 180 C while backflushing the trap with an inert gas be- tween 20 and 60 mL/min for 1.5 min.

  - While the trap is being desorbed into the gas chromatograph, empty the purging chamber using the sample introduction sy-

As  = Response for the parameter to be meas- ured.

Ais = Response for the internal standard.

Cis = Concentration of the internal standard.

11.2 Report results in g/L without correc- tion for recovery data. All QC data obtained should be reported with the sample results.

- Method Performance

  - The method detection limit (MDL) is defined as the minimum concentration of a substance that can be measured and reported with 99% confidence that the value is above zero. 1  The  MDL  concentrations  listed   in Table  1  were  obtained  using  reagent  water. 9

#### Pt. 136, App. A, Meth. 603

The MDL actually achieved in a given anal- ysis will vary depending on instrument sen- sitivity and matrix effects.

  - This method is recommended for the concentration range from the MDL to 1,000  MDL. Direct aqueous injection techniques should be used to measure concentration lev- els above 1,000 MDL.

  - In a single laboratory (Battelle-Co- lumbus), the average recoveries and standard deviations presented in Table 2 were ob- tained. 9 Seven replicate samples were ana- lyzed at each spike level.

References

- 40 CFR part 136, appendix B.

- Bellar,  T.A.,  and  Lichtenberg,  J.J. ‘‘De- termining   Volatile   Organics   at   Microgram- per-Litre-Levels   by   Gas   Chromatography,’’ Journal American Water Works Association, 66, 739 (1974).

- ‘‘Evaluate Test Procedures for Acrolein and Acrylonitrile,’’ Special letter report for EPA Project 4719–A, U.S. Environmental Protection Agency, Environmental Moni- toring and Support Laboratory, Cincinnati, Ohio 45268, 27 June 1979.

- ‘‘Carcinogens—Working With Carcino- gens,’’ Department of Health, Education, and Welfare, Public Health Service, Center for Disease Control, National Institute for Occu- pational Safety and Health, Publication No. 77–206, August 1977.

- ‘‘OSHA Safety and Health Standards, General Industry,’’ (29 CFR part 1910), Occu- pational Safety and Health Administration, OSHA 2206 (Revised, January 1976).

- ‘‘Safety in Academic Chemistry Labora- tories,’’ American Chemical Society Publica-

#### 40 CFR Ch. I (7–1–17 Edition)

tion,   Committee   on   Chemical   Safety,   3rd Edition, 1979.

- Provost,  L.P.,  and  Elder,  R.S.  ‘‘Interpre- tation   of   Percent   Recovery   Data,’’   American Laboratory, 15, 58–63 (1983).

- ‘‘Methods 330.4 (Titrimetric, DPD-FAS) and 330.5 (Spectrophotometric, DPD) for Chlorine, Total Residual,’’ Methods for Chemical Analysis of Water and Wastes, EPA–600/4–79–020, U.S. Environmental Pro- tection Agency, Environmental Monitoring and Support Laboratory, Cincinnati, Ohio 45268, March 1979.

- ‘‘Evaluation of Method 603 (Modified),’’ EPA–600/4–84–ABC, National Technical Infor- mation Service, PB84–, Springfield, Virginia 22161, Nov. 1984.

TABLE 1—CHROMATOGRAPHIC CONDITIONS AND

METHOD DETECTION LIMITS

| Parameter | Retention time (min) | Method detection limit (g/L) |
| --- | --- | --- |
|  | Column 1 | Column 2 |  |
| Acrolein .................... Acrylonitrile .............. | 10.6 12.7 | 8.2 9.8 | 0.7 0.5 |

Column 1 conditions: Porapak-QS (80/100 mesh) packed in a 10 ft 2 mm ID glass or stainless steel column with helium carrier gas at 30 mL/min flow rate. Column temperature held isothermal at 110 C for 1.5 min (during desorption), then heated as rapidly as possible to 150 C and held for 20 min; column bakeout at 190 C for 10 min. 9

Column 2 conditions: Chromosorb 101 (60/80  mesh) packed in a 6 ft. 0.1 in. ID glass or stainless steel column with helium carrier gas at 40 mL/min flow rate. Column tem- perature held isothermal at 80 C for 4 min, then programmed at 50 C/min to 120 C and held for 12 min.

TABLE 2—SINGLE LABORATORY ACCURACY AND PRECISION—METHOD 603

| Parameter | Sample matrix | Spike conc. (g/L) | Average recovery (g/L) | Standard deviation (g/L) | Average percent recovery |
| --- | --- | --- | --- | --- | --- |
| Acrolein ................................................................................................. | RW | 5.0 | 5.2 | 0.2 | 104 |
|  | RW | 50.0 | 51.4 | 0.7 | 103 |
|  | POTW | 5.0 | 4.0 | 0.2 | 80 |
|  | POTW | 50.0 | 44.4 | 0.8 | 89 |
|  | IW | 5.0 | 0.1 | 0.1 | 2 |
|  | IW | 100.0 | 9.3 | 1.1 | 9 |
| Acrylonitrile ............................................................................................ | RW | 5.0 | 4.2 | 0.2 | 84 |
|  | RW | 50.0 | 51.4 | 1.5 | 103 |
|  | POTW | 20.0 | 20.1 | 0.8 | 100 |
|  | POTW | 100.0 | 101.3 | 1.5 | 101 |
|  | IW | 10.0 | 9.1 | 0.8 | 91 |
|  | IW | 100.0 | 104.0 | 3.2 | 104 |

RW = Reagent water.

POTW = Prechlorination secondary effluent from a municipal sewage treatment plant. IW = Industrial wastewater containing an unidentified acrolein reactant.

TABLE 3—CALIBRATION AND QC ACCEPTANCE CRITERIA—METHOD 603 A

| Parameter | Range for Q (g/L) | Limit for S (g/L) | Range for X (g/L) | Range for P, Ps (%) |
| --- | --- | --- | --- | --- |
| Acrolein ..................................................................................................... | 45.9–54.1 | 4.6 | 42.9–60.1 | 88–118 |

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 603

TABLE 3—CALIBRATION AND QC ACCEPTANCE CRITERIA—METHOD 603 A—Continued

| Parameter | Range for Q (g/L) | Limit for S (g/L) | Range for X (g/L) | Range for P, Ps (%) |
| --- | --- | --- | --- | --- |
| Acrylonitrile ................................................................................................ | 41.2–58.8 | 9.9 | 33.1–69.9 | 71–135 |

a = Criteria were calculated assuming a QC check sample concentration of 50 g/L. 9

Q = Concentration measured in QC check sample, in g/L (Section 7.5.3).

s = Standard deviation of four recovery measurements, in g/L (Section 8.2.4). X = Average recovery for four recovery measurements, in g/L (Section 8.2.4). P, Ps  = Percent recovery measured (Section 8.3.2, Section 8.4.2).

#### Pt. 136, App. A, Meth. 603

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 603

Pt. 136, App. A, Meth. 604

40 CFR Ch. I (7–1–17 Edition)

METHOD 604—PHENOLS

- Scope and Application

  - This method covers the determination of phenol and certain substituted phenols. The following parameters may be deter- mined by this method:

| Parameter | STORET No. | CAS No. |
| --- | --- | --- |
| 4-Chloro-3-methylphenol ................. | 34452 | 59–50–7 |
| 2–-Chlorophenol .............................. | 34586 | 95–57–8 |
| 2,4-Dichlorophenol .......................... | 34601 | 120–83–2 |
| 2,4-Dimethylphenol ......................... | 34606 | 105–67–9 |
| 2,4-Dinitrophenol ............................. | 34616 | 51–28–5 |
| 2-Methyl-4,6-dinitrophenol .............. | 34657 | 534–52–1 |
| 2-Nitrophenol ................................... | 34591 | 88–75–5 |
| 4-Nitrophenol ................................... | 34646 | 100–02–7 |
| Pentachlorophenol .......................... | 39032 | 87–86–5 |
| Phenol ............................................. | 34694 | 108–95–2 |
| 2,4,6-Trichlorophenol ...................... | 34621 | 88–06–2 |

  - This is a flame ionization detector gas chromatographic  (FIDGC)  method   applicable to the determination of the compounds listed above in municipal and  industrial  discharges as provided under 40 CFR 136.1. When this method   is   used   to   analyze   unfamiliar   sam-

ples for any or all of the compounds above, compound identifications should be sup- ported by  at  least  one  additional  qualitative technique. This method describes analytical conditions for derivatization, cleanup, and electron capture detector gas chroma- tography (ECDGC) that can be used to con- firm measurements made by FIDGC. Method 625 provides gas chromatograph/mass spec- trometer (GC/MS) conditions appropriate for the qualitative and  quantitative  confirma- tion of results for all of the parameters list- ed above, using the extract produced by this method.

  - The method detection limit (MDL, de- fined in Section 14.1) 1 for each parameter is listed in Table 1. The MDL for a specific wastewater may differ from those listed, de- pending upon the nature of interferences  in the  sample  matrix.  The  MDL  listed  in  Table

1 for each parameter was achieved with a flame ionization detector (FID). The MDLs that were achieved when the derivatization cleanup and electron capture detector (ECD) were employed are presented in Table 2.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 604

  - Any modification of this method,  be- yond those expressly permitted, shall be con- sidered as a major modification subject to application and approval of alternate test procedures under 40 CFR 136.4 and 136.5.

  - This method is restricted to use by or under the supervision of analysts experi- enced in the use of a gas chromatograph and in the interpretation of gas chromatograms. Each analyst must demonstrate  the  ability to generate acceptable results with this method using the procedure described in Sec- tion 8.2.

- Summary of Method

  - A measured volume of sample, ap- proximately 1-L, is acidified and extracted with methylene chloride using a separatory funnel. The methylene chloride extract  is dried and exchanged to 2-propanol during concentration to a volume of 10 mL or less. The extract is separated by gas chroma- tography and the phenols are then measured with an FID. 2

  - A preliminary sample wash under basic conditions can be employed for samples having high general organic and organic base interferences.

  - The method also provides for a derivatization and column chromatography cleanup procedure to aid  in  the  elimination of interferences. 2 3 The derivatives are ana- lyzed  by  ECDGC.

- Interferences

  - Method interferences may be caused by contaminants in solvents, reagents, glass- ware, and other sample processing hardware that lead to discrete artifacts and/or ele- vated baselines in gas chromatograms. All of these materials must be routinely dem- onstrated to be free from interferences under the conditions of the analysis by running laboratory reagent blanks as described in Section 8.1.3.

    - Glassware must be scrupulously cleaned. 4 Clean all glassware as soon as pos- sible after use by rinsing with the last sol- vent used in it. Solvent rinsing should be fol- lowed by detergent washing with hot water, and rinses with tap water and distilled water. The glassware should then be drained dry, and heated in a muffle furnace at 400 C for 15 to 30 min. Some thermally stable ma- terials, such as PCBs, may not be eliminated by this treatment. Solvent rinses with ace- tone and pesticide quality hexane may be substituted for the muffle furnace heating. Thorough rinsing with such solvents usually eliminates PCB interference. Volumetric ware should not be heated in a muffle fur- nace. After drying and cooling, glassware should be sealed and stored in a clean envi- ronment to prevent any accumulation of dust or other contaminants. Store inverted or capped with aluminum foil.

    - The use of high purity reagents and solvents helps to minimize interference prob- lems. Purification of solvents  by  distillation in all-glass systems may be required.

  - Matrix interferences may be caused by contaminants that are coextracted from the sample. The extent of matrix interferences will vary considerably from source to source, depending upon the nature and diversity  of the industrial complex or municipality being sampled. The derivatization cleanup proce- dure in Section 12 can be used to overcome many of these interferences, but unique sam- ples may require additional cleanup ap- proaches to achieve the MDL listed in Tables 1 and 2.

  - The basic sample wash (Section 10.2) may cause significantly reduced recovery of phenol and 2,4-dimethylphenol. The analyst must recognize that results obtained under these conditions are minimum concentra- tions.

- Safety

  - The toxicity or carcinogenicity of each reagent used in this mothod has not been precisely defined; however, each chem- ical compound should be treated as a poten- tial health hazard. From this viewpoint, ex- posure to these chemicals must be reduced to the lowest possible level by whatever means available. The laboratory is responsible for maintaining a current awareness file of OSHA regulations regarding the safe han- dling of the chemicals specified in this meth- od. A reference file of material data handling sheets should also be made available to all personnel involved in the chemical analysis. Additional references to laboratory safety are available and have been identified 5 7 for the information of analyst.

  - Special care should be taken in han- dling pentafluorobenzyl bromide, which is a lachrymator, and 18-crown-6-ether, which is highly   toxic.

- Apparatus and Materials

  - Sampling equipment, for discrete or composite  sampling.

    - Grab sample bottle—1–L or 1-qt, amber glass, fitted with a screw cap lined with Teflon. Foil may be substituted for Tef- lon if the sample is not corrosive. If amber bottles are not available, protect samples from light. The bottle and cap liner must be washed, rinsed with acetone or methylene chloride, and dried before use to minimize contamination.

    - Automatic sampler (optional)—The sampler must incorporate glass sample con- tainers for the collection of a minimum of 250 mL of sample. Sample containers must be kept refrigerated at 4 C and protected from light during compositing. If the sampler uses a peristaltic pump, a minimum length of compressible  silicone  rubber  tubing  may  be

#### Pt. 136, App. A, Meth. 604

used. Before use, however, the compressible tubing should be thoroughly rinsed with methanol, followed by repeated rinsings with distilled water to minimize the potential for contamination of the sample. An integrating flow meter is required to collect flow propor- tional composites.

  - Glassware (All specifications are sug- gested. Catalog numbers are included for il- lustration only.):

    - Separatory funnel—2–L, with Teflon stopcock.

    - Drying column—Chromatographic column, 400 mm long 19 mm ID, with coarse frit  filter  disc.

    - Chromatographic column—100 mm long 10 mm ID, with Teflon stopcock.

    - Concentrator tube, Kuderna-Dan- ish—10-mL, graduated (Kontes K–570050–1025 or equivalent). Calibration must  be  checked at the volumes employed in the test. Ground glass stopper is used to prevent evaporation of  extracts.

    - Evaporative flask, Kuderna-Danish— 500-mL (Kontes K–570001–0500 or equivalent). Attach  to  concentrator  tube  with  springs.

    - Snyder column, Kuderna-Danish— Three-ball macro (Kontes K–503000–0121 or equivalent).

    - Snyder column, Kuderna-Danish— Two-ball micro (Kontes K–569001–0219 or equivalent).

    - Vials—10 to 15-mL, amber glass, with Teflon-lined screw cap.

    - Reaction flask—15 to 25-mL round bottom flask, with standard tapered joint, fitted with a water-cooled condenser and U- shaped drying tube containing granular cal- cium  chloride.

  - Boiling chips—Approximately 10/40 mesh. Heat to 400 C for 30 min or Soxhlet ex- tract  with  methylene  chloride.

  - Water bath—Heated, with concentric ring cover, capable of temperature control (2 C). The bath should be used in a hood.

  - Balance—Analytical, capable of accu- rately weighting 0.0001 g.

  - Gas chromatograph—An analytical system complete  with  a  temperature  pro- grammable gas chromatograph suitable for on-column injection and all required acces- sories including syringes, analytical  col- umns, gases, detector, and strip-chart re- corder. A data system is recommended for measuring peak areas.

5.6.1    Column   for   underivatized   phenols—

1.8 m long 2 mm ID glass, packed with 1% SP–1240DA on Supelcoport (80/100 mesh) or equivalent. This column was used to  develop the method performance statements in Sec- tion 14. Guidelines for the use of alternate column  packings  are  provided   in   Section 11.1.

    - Column  for  derivatized  phenols—1.8 m long 2 mm ID glass, packed with 5% OV– 17 on Chromosorb W-AW-DMCS (80/100 mesh) or  equivalent.  This  column  has  proven  effec-

#### 40 CFR Ch. I (7–1–17 Edition)

tive in the analysis of wastewaters for derivatization products of the parameters listed in the scope (Section 1.1), and was used to develop the method performance state- ments in Section 14. Guidelines for the use of alternate column packings are provided in Section 11.1.

    - Detectors—Flame ionization and electron capture detectors. The FID is used when determining the parent phenols. The ECD is used when determining the derivatized phenols. Guidelines for the use of alternatve detectors are provided in Section 11.1.

- Reagents

  - Reagent water—Reagent water is de- fined as a water in which an  interferent  is not observed at the  MDL  of  the  parameters of  interest.

  - Sodium hydroxide solution (10 N)— Dissolve 40 g of NaOH (ACS) in reagent water and dilute to 100 mL.

  - Sodium hydroxide solution (1 N)—Dis- solve 4 g of NaOH (ACS) in reagent water and dilute to 100 mL.

  - Sodium sulfate—(ACS) Granular, an- hydrous. Purify by heating at 400 C for 4 h in a shallow tray.

  - Sodium thiosulfate—(ACS) Granular.

  - Sulfuric acid (1 + 1)—Slowly, add  50 mL of  H2SO4 (ACS, sp.  gr.  1.84) to  50  mL of reagent water.

  - Sulfuric acid (1 N)—Slowly, add 58 mL of H2SO4 (ACS, sp. gr. 1.84) to reagent water and dilute to 1 L.

  - Potassium carbonate—(ACS) Pow- dered.

  - Pentafluorobenzyl	bromide	(a- Bromopentafluorotoluene)—97% minimum purity.

NOTE: This chemical is a lachrymator. (See Section 4.2.)

6.10      18-crown-6-ether	(1,4,7,10,13,16-

Hexaoxacyclooctadecane)—98% minimum purity.

NOTE: This chemical is highly toxic.

  - Derivatization reagent—Add 1 mL of pentafluorobenzyl bromide and 1 g of 18- crown-6-ether to a 50-mL volumetric flask and dilute to volume with 2-propanol. Pre- pare fresh weekly. This operation should be carried out in a hood. Store at 4 C and pro- tect  from  light.

  - Acetone, hexane, methanol, meth- ylene chloride, 2-propanol, toluene—Pes- ticide quality or equivalent.

  - Silica gel—100/200 mesh, Davison, grade-923 or equivalent. Activate at 130 C overnight and store in a desiccator.

  - Stock    standard    solutions    (1.00    g/

L)—Stock standard solutions may be pre- pared from pure standard materials or pur- chased as certified solutions.

    - Prepare stock standard solutions by accurately weighing about 0.0100 g of pure material.  Dissolve  the  material  in  2-propanol

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 604

and dilute to volume in a 10-mL volumetric flask. Larger volumes can be used at the con- venience of the analyst. When compound pu- rity is assayed to be 96% or greater, the weight can be used without correction to cal- culate the concentration of the stock stand- ard. Commercially prepared stock standards can be used at any concentration if they are certified by the manufacturer or by an inde- pendent source.

    - Transfer the stock standard solu- tions into Teflon-sealed screw-cap bottles. Store at 4 C and protect from light. Stock standard solutions should be checked fre- quently for signs of degradation or evapo- ration, especially just prior to preparing calibration standards from them.

    - Stock standard solutions must be replaced after six months, or sooner if com- parison with check standards indicates a problem.

6.15 Quality control check sample con- centrate—See Section 8.2.1.

- Calibration

  - To calibrate the FIDGC for the anaylsis of underivatized phenols, establish gas chromatographic operating conditions equivalent to those given in Table 1. The gas chromatographic system can be calibrated using the external standard technique (Sec- tion 7.2) or the internal standard technique (Section 7.3).

  - External standard calibration proce- dure for FIDGC:

    - Prepare calibration standards at a minimum of three concentration levels  for each parameter of interest by adding vol- umes of one or more stock standards to a volumetric flask and diluting to volume with 2-propanol. One of the external standards should be at a concentration near, but above, the MDL (Table 1) and the other concentra- tions should correspond to the expected range of concentrations found in real sam- ples or should define the working range of the detector.

    - Using injections of 2 to 5 l, analyze

each calibration standard according to Sec- tion 11 and tabulate peak height or area re- sponses against  the mass injected. The re- sults can be used to prepare a calibration curve for each compound. Alternatively, if the ratio of response to amount injected (calibration factor) is a constant over the working range (<10% relative standard devi- ation, RSD), linearity through the origin can be assumed and the average ratio or calibra- tion factor can be used in place of a calibra- tion curve.

  - Internal standard calibration proce- dure for FIDGC—To use this approach, the analyst must select one or more internal standards that are similar in analytical be- havior to the compounds of interest. The an- alyst must further demonstrate that the measurement of the internal standard is not

affected by method or matrix interferences. Because of these limitations, no internal standard can be suggested that is applicable to all samples.

    - Prepare calibration standards at a minimum of three concentration levels  for each parameter of interest by adding vol- umes of one or more stock standards to a volumetric flask. To each calibration stand- ard, add a known constant amount of one or more internal standards, and dilute to vol- ume with 2-propanol. One of the standards should be at a concentration near, but above, the MDL and the other concentrations should correspond to the expected range of concentrations found in real samples or should define the working range of the detec- tor.

    - Using injections of 2 to 5 L, analyze

each calibration standard according to Sec- tion 11 and tabulate peak height or area re- sponses against concentration for each com- pound and internal standard. Calculate re- sponse factors (RF) for each compound using Equation 1.

RF = (As)(Cis (Ais)(Cs)

Equation   1

where:

As  = Response for the parameter to be meas- ured.

Ais = Response for the internal standard.

Cis  = Concentration of the internal standard (g/L).

Cs   =  Concentration  of  the  parameter  to  be measured (g/L).

If the RF value over the working range is a constant (<10% RSD), the RF can be as- sumed to be invariant and the average RF can be used for calculations. Alternatively, the results can be used to plot a calibration curve of response ratios, As/Ais, vs. RF.

  - The  working  calibration  curve,  cali-

bration factor, or RF must be verified on each working day by the measurement of one or more calibration standards. If the re- sponse for any parameter varies from the predicted response by more than 15%, a new calibration curve must be prepared for that compound.

  - To calibrate the ECDGC for the anal- ysis of phenol derivatives, establish gas chromatographic operating conditions equiv- alent to those given in Table 2.

    - Prepare calibration standards at a minimum of three concentration levels  for each parameter of interest by adding vol- umes of one or more stock standards to a volumetric flask and diluting to volume with 2-propanol. One of the external standards should be at a concentration near, but above, the MDL (Table 2) and the other concentra- tions should correspond to the expected range of concentrations found in real sam- ples or should define the working range of the detector.

#### Pt. 136, App. A, Meth. 604

    - Each time samples are to be derivatized, simultaneously  treat  a  1-mL  ali- quot of each calibration standard as de- scribed in Section 12.

    - After   derivatization,   analyze   2   to   5

L of each column eluate collected according to the method beginning in Section 12.8 and tabulate peak height or  area  responses against the calculated equivalent mass of underivatized phenol injected.  The  results can be used to prepare a calibration curve for each compound.

7.6 Before using any cleanup  procedure, the analyst must process a series of calibra- tion standards through the procedure to vali- date elution patterns and the absence of interferences from the reagents.

- Quality Control

  - Each laboratory that uses this method is required to operate a formal quality  con- trol program. The minimum requirements of this program consist of an initial demonstra- tion of laboratory capability and an ongoing analysis of spiked samples to evaluate and document data quality. The laboratory must maintain records to document the quality of data that is generated. Ongoing data quality checks are compared with established per- formance criteria to determine if the results of analyses meet the performance character- istics of the method. When results of sample spikes indicate atypical method perform- ance, a quality control check  standard  must be analyzed to confirm that the measure- ments were performed in an in-control mode of operation.

    - The analyst must make an initial, one-time, demonstration of the ability to generate acceptable accuracy and precision with this method. This  ability  is  established as described in Section 8.2.

    - In recognition of advances that are occurring in chromatography, the analyst is permitted certain  options  (detailed  in  Sec- tions 10.6 and 11.1) to improve the separa- tions or lower the cost of measurements. Each time such a modification is  made  to the method, the analyst is required to repeat the procedure in Section 8.2.

    - Before processing any samples the analyst must analyze a  reagent  water  blank to demonstrate that interferences from the analytical system and glassware are under control. Each time a set of samples is ex- tracted or reagents are changed a reagent water blank must be processed as a safe- guard  against  laboratory  contamination.

    - The laboratory must, on an ongoing basis, spike and analyze a minimum of 10% of all samples to monitor and evaluate lab- oratory data quality. This procedure is de- scribed in Section 8.3.

    - The laboratory must, on an ongoing basis, demonstrate through the analyses of quality control  check standards  that  the op- eration of the measurement system is in con-

#### 40 CFR Ch. I (7–1–17 Edition)

trol. This procedure is described in Section

8.4. The frequency of the check standard analyses is equivalent to 10% of all samples analyzed but may be reduced if spike recov- eries from samples (Section 8.3) meet all specified quality control criteria.

    - The laboratory must maintain per- formance records to document the quality of data that is generated. This procedure is de- scribed in Section 8.5.

  - To establish the ability to generate acceptable accuracy and precision, the ana- lyst must perform the following operations.

    - A quality control (QC) check sample concentrate is required containing each pa- rameter of interest at a concentration of 100

g/mL in 2-propanol. The QC check sample concentrate must be obtained from the U.S. Environmental Protection Agency, Environ- mental Monitoring and Support Laboratory in Cincinnati, Ohio, if available. If not avail- able from that source, the QC check sample concentrate must be obtained from another external source. If not available from either source above, the QC check sample con- centrate must be prepared by the laboratory using stock standards prepared independ- ently from those used for calibration.

    - Using a pipet, prepare QC check sam- ples at a concentration of 100 g/L by adding

1.00 mL of QC check sample concentrate to each of four 1-L aliquots of reagent water.

    - Analyze the well-mixed QC check samples according to the  method  beginning in Section 10.

    - Calculate the average recovery (X¯ ) in

g/L, and the standard deviation of the re- covery (s) in g/L, for each parameter using the four results.

    - For each parameter compare s and X¯

with the corresponding acceptance criteria for   precision   and   accuracy,   respectively,

found in Table 3. If s and X¯  for all param-

eters of interest meet the acceptance cri- teria, the system performance is acceptable and analysis of actual samples can begin. If

any individual s exceeds the precision limit or any individual X¯  falls outside the range

for accuracy, the system performance is un- acceptable for that parameter.

NOTE: The large number of parameters in Talbe 3 present  a  substantial  probability that one or more will fail at least one of the acceptance criteria when all parameters are analyzed.

    - When one or more of the parameters tested fail at least one of the acceptance cri- teria, the analyst must proceed according to Section 8.2.6.1 or 8.2.6.2.

      - Locate and correct the source of the problem and repeat the test for all pa- rameters of interest beginning with Section 8.2.2.

      - Beginning with Section 8.2.2, repeat the test only for those  parameters  that failed to meet criteria. Repeated failure, however,   will   confirm   a   general   problem

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 604

with the measurement system. If this occurs, locate and correct the source of the problem and repeat the test for all compounds of in- terest beginning with Section 8.2.2.

  - The laboratory must, on an ongoing basis, spike at least 10% of the samples from each sample site being monitored to assess accuracy. For laboratories analyzing one to ten samples per month, at least one spiked sample per month is required.

    - The concentration of the spike in the sample should be determined as follows:

      - If, as in compliance monitoring, the concentration of a specific parameter in the sample is being checked against a regu- latory concentration limit, the spike should be at that limit or 1 to 5 times higher than the background concentration determined in Section 8.3.2, whichever concentration would be larger.

      - If the concentration of a specific parameter in the sample  is  not  being checked against a limit specific to that pa- rameter, the spike should be at 100 g/L or 1 to 5  times  higher than  the  background  con- centration determined in Section 8.3.2, whichever concentration would be larger.

      - If it is impractical to determine background levels before spiking (e.g., max- imum holding times will be exceeded), the spike concentration should be (1) the regu- latory concentration limit, if any,  or,  if none, (2) the larger of either 5 times higher than the expected background concentration or 100 g/L.

    - Analyze one sample aliquot to deter- mine the background concentration (B) of each parameter. If necessary, prepare a new QC check sample concentrate (Section 8.2.1) appropriate for the background concentra- tions in the sample. Spike a second sample aliquot with 1.0 mL of the QC check sample concentrate and analyze it to determine the concentration after spiking (A) of each pa- rameter. Calculate each percent recovery (P) as 100(A¥B)%/T, where T is the known true value of the spike.

    - Compare the percent recovery (P) for each parameter with the corresponding QC acceptance criteria found in Table 3. These acceptance criteria were calculated to in- clude an allowance for error in measurement of both the background and spike concentra- tions, assuming a spike  to  background  ratio of 5:1. This error will be accounted for to the extent that the analyst’s spike to back- ground ratio approaches 5:1. 8 If spiking was performed at a concentration lower than 100

g/L, the analyst must use either the QC ac- ceptance criteria in Table 3, or optional QC acceptance criteria calculated  for the  spe- cific spike concentration. To calculate op- tional acceptance criteria for the recovery of a parameter: (1) Calculate accuracy (X) using the equation in Table 4,  substituting the spike concentration (T) for C; (2) cal- culate  overall  precision  (S)  using  the  equa-

tion in Table 4, substituting Xfor X¯ ; (3) cal- culate the range for recovery at the spike concentration as (100 X/T)2.44(100 S/T)%. 8

    - If any individual P falls outside the designated range for recovery, that param- eter has failed the acceptance criteria. A check standard containing each parameter that failed the criteria must be analyzed as described in Section 8.4.

  - If any parameter fails the acceptance criteria for recovery in Section 8.3, a QC check standard containing each parameter that failed must be prepared and analyzed.

NOTE: The frequency for the required anal- ysis of a QC check standard will depend upon the number of parameters being simulta- neously tested, the complexity of the sample matrix, and the performance of the labora- tory.

    - Prepare the QC check standard by adding 1.0 mL of QC check sample con- centrate (Section 8.2.1 or 8.3.2) to 1 L of rea- gent water. The QC check standard needs only to contain the parameters that failed criteria in the test in Section 8.3.

    - Analyze the QC check standard to determine the concentration measured (A) of each parameter. Calculate each percent re- covery (Ps) as 100 (A/T)%, where T is the true value of the standard concentration.

    - Compare the percent recovery (Ps) for each parameter with the corresponding QC acceptance criteria found in Table 3. Only parameters that failed the test in Section 8.3 need to be compared with these  criteria.  If the recovery of any such parameter falls out- side the designated range, the laboratory performance for that parameter is judged to be out of control, and the problem must be immediately identified and corrected. The analytical result for that parameter in the unspiked sample is suspect  and may not  be reported for regulatory compliance purposes.

8.5 As part of the QC program for the lab- oratory, method accuracy for wastewater samples must be assessed and records must be maintained. After the analysis of five spiked wastewater samples as in Section 8.3,

calculate  the  average  percent  recovery  (P¯ )

and the standard deviation of the percent re- covery (sp). Express the accuracy assessment

as a percent recovery interval from P¯ ¥2sp to P¯ + 2sp. If P¯ = 90% and sp = 10%, for example,

the accuracy interval is expressed as 70– 110%. Update the accuracy  assessment  for each parameter on a regular basis (e.g. after each five to  ten  new  accuracy  measure- ments).

8.6. It is recommended that the labora- tory adopt additional quality assurance practices for use with this method. The spe- cific practices that are most productive de- pend upon the needs of the  laboratory  and the nature of the samples. Field duplicates may be analyzed to assess the  precision  of the    environmental    measurements.    When

#### Pt. 136, App. A, Meth. 604

doubt exists over the identification of a peak on the chromatogram, confirmatory tech- niques such as gas chromatography with a dissimilar column, specific element  detector, or mass spectrometer must be used. When- ever possible, the laboratory should analyze standard reference materials and participate in relevant performance evaluation studies.

- Sample Collection, Preservation, and Handling

  - Grab samples must be collected  in glass containers. Conventional sampling practices 9 should be followed, except  that the bottle must not be prerinsed with sample before collection. Composite samples should be collected in refrigerated  glass  containers in accordance with the requirements of the program. Automatic sampling equipment must be as free as possible of Tygon tubing and other potential sources of contamina- tion.

  - All samples must be iced or refrig- erated at 4 C from the time of collection until extraction. Fill the sample bottles and, if residual chlorine is present, add 80 mg of sodium thiosulfate per liter of sample and mix well. EPA Methods 330.4 and 330.5 may be used for measurement of residual chlo- rine. 10 Field test kits are available for this purpose.

  - All samples must be extracted within 7 days of collection and completely analyzed within 40 days of extraction. 2

- Sample Extraction

  - Mark the water meniscus on the side of sample bottle for later determination of sample volume. Pour the entire sample into a 2-L separatory funnel.

  - For samples high in organic content, the analyst may solvent wash the sample at basic pH as prescribed in Sections 10.2.1 and

10.2.2 to remove potential method inter- ferences. Prolonged or exhaustive contact with solvent during the wash may result  in low recovery of some of the phenols, notably phenol and 2,4-dimethylphenol. For rel- atively clean samples, the wash should be omitted and the extraction, beginning with Section 10.3, should be followed.

    - Adjust the pH of the sample to 12.0 or greater with sodium hydroxide solution.

    - Add 60 mL of methylene chloride to the sample by shaking the funnel for 1 min with periodic venting to release excess pres- sure. Discard the solvent layer. The wash can be repeated up to two additional times if significant color is being removed.

  - Adjust the sample to a pH of 1 to  2 with  sulfuric  acid.

  - Add 60 mL of methylene chloride  to the sample bottle, seal, and shake 30 s to rinse the inner surface. Transfer the solvent to the separatory funnel and extract the sample by shaking the funnel for 2 min. with

#### 40 CFR Ch. I (7–1–17 Edition)

periodic venting to release excess pressure. Allow the organic layer to separate from the water phase for a minimum of 10 min. If the emulsion interface between layers is more than one-third the volume of the solvent layer, the analyst must employ mechanical techniques to complete the phase separation. The optimum technique depends upon the sample, but may include  stirring,  filtration of the emulsion through glass wool, cen- trifugation, or other physical methods. Col- lect the methylene chloride extract in a 250- mL Erlenmeyer flask.

  - Add a second 60-mL volume of meth- ylene chloride to the sample bottle and re- peat the extraction procedure a second time, combining the extracts in the Erlenmeyer flask. Perform a third extraction in the same manner.

  - Assemble a Kuderna-Danish (K-D) concentrator by attaching a 10-mL concen- trator tube to a 500-mL evaporative flask. Other concentration devices or  techniques may be used in place of the K-D concentrator if the requirements of Section 8.2 are met.

  - Pour the combined extract through a solvent-rinsed drying column containing about 10 cm of anhydrous sodium sulfate, and collect the extract in the K-D concen- trator. Rinse the Erlenmeyer flask and col- umn with 20 to 30 mL of methylene chloride to complete the quantitative transfer.

  - Add one or two clean boiling chips to the evaporative flask and attach a three-ball Snyder column. Prewet the Snyder  column by adding about 1 mL of methylene chloride to the top. Place the K-D apparatus on a hot water bath (60 to 65 C) so that the concen- trator tube is partially immersed in the hot water, and the entire lower rounded surface of the flask is bathed with hot vapor. Adjust the vertical position of the apparatus  and the water temperature as required to com- plete the concentration in 15 to  20  min.  At the proper rate of distillation the balls of the column will actively chatter but the cham- bers will not flood with condensed solvent. When the apparent volume of liquid reaches 1 mL, remove the K-D apparatus and allow it to drain and cool for at least 10 min.

  - Increase the temperature of the hot water bath to 95 to 100 C. Remove the Synder column and rinse the flask and its lower joint into the concentrator tube with 1 to 2 mL of 2-propanol. A 5-mL syringe is rec- ommended for this operation. Attach a two- ball micro-Snyder column to the concen- trator tube and prewet the column by adding about 0.5 mL of 2-propanol to the top. Place the micro-K-D apparatus on  the  water  bath so that the concentrator tube is partially immersed in the hot water. Adjust the vertical position of the apparatus and the water temperature as required to complete concentration in 5 to 10 min. At the proper rate of distillation the balls of the  column will  actively  chatter  but  the  chambers  will

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 604

not flood. When the apparent volume of liq- uid reaches 2.5 mL, remove the K-D appa- ratus and allow it to drain and cool for  at least 10 min. Add an additional 2 mL of 2- propanol through the top of the  micro-Sny- der column and resume concentrating as be- fore. When the apparent volume of liquid reaches 0.5 mL, remove the K-D apparatus and allow it to drain and cool for at least 10 min.

  - Remove the micro-Snyder column and rinse its lower joint into the concen- trator tube with a minimum amount of 2- propanol. Adjust the extract volume to 1.0 mL. Stopper the concentrator tube and store refrigerated at 4 C if further processing will not be performed immediately. If the extract will be stored longer than two days, it should be transferred to a Teflon-sealed screw-cap vial. If the sample extract requires no fur- ther cleanup, proceed with FIDGC analysis (Section 11). If the sample requires further cleanup, proceed to Section 12.

  - Determine the original sample vol- ume by refilling the sample bottle to the mark and transferring the liquid to  a  1000- mL graduated cylinder. Record the sample volume to the nearest 5 mL.

- Flame Ionization Detector Gas Chromatography

  - Table 1 summarizes the recommended operating conditions for the gas chro- matograph. Included in this table are reten- tion times and MDL that can be achieved under these conditions. An example of the separations achieved by  this  column  is shown in Figure 1. Other packed or capillary (open-tubular) columns, chromatographic conditions, or detectors may be used if the requirements of Section 8.2 are met.

  - Calibrate the system daily as de- scribed in Section 7.

  - If the internal standard calibration procedure is used, the internal standard must be added to the sample extract and mixed thoroughly immediately before injec- tion into the gas chromatograph.

  - Inject  2  to  5  L  of  the  sample  extract

or standard into the gas chromatograph using the solvent-flush technique. 11 Smaller (1.0 L) volumes may be injected if auto- matic devices are employed. Record the vol- ume injected to the nearest 0.05 L, and the resulting peak size in area or peak height units.

  - Identify the parameters in the sample by comparing the retention times of the peaks in the sample chromatogram with those of the peaks in standard chromatograms. The width of the retention time window used to make identifications should be based upon measurements of ac- tual retention time variations of standards over the course of a day. Three times the standard deviation of a retention time for a compound may be used to calculate a sug-

gested window size; however, the experience of the analyst should weigh heavily in the interpretation of chromatograms.

  - If the response for a peak exceeds the working range of the system, dilute the ex- tract and reanalyze.

  - If the measurement of the peak re- sponse is prevented by the presence of inter- ferences, an alternative gas chromatographic procedure is required. Section 12 describes a derivatization and column chromatographic procedure which  has  been tested  and  found to be a practical means of analyzing phenols in  complex  extracts.

- Derivatization and Electron Capture Detector Gas Chromatography

  - Pipet a 1.0-mL aliquot of the 2-pro- panol solution of standard or sample extract into a glass reaction vial. Add 1.0 mL of derivatizing reagent (Section 6.11). This amount of reagent is sufficient to derivatize a solution whose total phenolic content does not exceed 0.3 mg/mL.

  - Add about 3 mg of potassium car- bonate to the solution and shake gently.

  - Cap the mixture and heat it for 4 h at 80 C in a hot water bath.

  - Remove the solution from the hot water bath and allow it to cool.

  - Add 10 mL of hexane to the reaction flask and shake vigorously for 1 min. Add 3.0 mL of distilled, deionized water to the reac- tion flask  and  shake  for  2  min.  Decant  a  por- tion of the organic layer into a concentrator tube and cap with a glass stopper.

  - Place 4.0 g of silica gel into a chromatographic column. Tap the column to settle the silica gel and add about 2 g of an- hydrous sodium sulfate to the top.

  - Preelute the column with 6 mL of hexane. Discard the eluate and just prior to exposure of the sodium sulfate layer  to  the air, pipet onto the column 2.0  mL  of  the hexane solution (Section 12.5) that contains the derivatized sample or standard. Elute the column with 10.0 mL of hexane  and  discard the  eluate.  Elute  the  column,  in  order,  with:

10.0 mL of 15% toluene in hexane (Fraction 1); 10.0 mL of 40% toluene in hexane (Frac- tion 2); 10.0 mL of 75% toluene in hexane (Fraction 3); and 10.0 mL of 15% 2-propanol in toluene (Fraction 4). All elution  mixtures are prepared on a volume: volume basis. Elution patterns for the phenolic derivatives are shown in Table 2. Fractions may be com- bined as desired, depending upon the specific phenols  of  interest  or  level  of  interferences.

  - Analyze the fractions  by  ECDGC. Table 2 summarizes the recommended oper- ating conditions for the gas chromatograph. Included in this table are retention times and MDL that can be achieved under these conditions. An example of the separations achieved by this column  is  shown  in  Figure 2.

#### Pt. 136, App. A, Meth. 604

40 CFR Ch. I (7–1–17 Edition)

  - Calibrate  the   system   daily   with   a minimum  of  three  aliquots  of  calibration

where:

Equation   4

standards, containing each of the phenols of

interest   that   are   derivatized   according   to Section 7.5.

  - Inject  2  to  5  L  of  the  column  frac-

tions into the gas chromatograph using the solvent-flush technique. Smaller (1.0 L) vol- umes can be injected if automatic  devices are employed. Record the volume injected to the nearest 0.05 L, and the resulting  peak size in area or peak height units. If the peak response exceeds the linear range of the sys- tem, dilute the extract and reanalyze.

- Calculations

  - Determine the concentration of indi- vidual compounds in the sample analyzed by FIDGC (without derivatization) as indicated below.

    - If the external standard calibration procedure is used, calculate the amount of material injected from the peak response using the calibration curve or calibration factor determined in Section 7.2.2. The con- centration in the sample can be calculated from Equation 2.

AVt 

## Concentration (g/L) 

Vi Vs 

Equation   2

where:

A = Amount of material injected (ng). Vi = Volume of extract injected (L). Vt = Volume of total extract (L).

Vs = Volume of water extracted (mL).

    - If the internal standard calibration procedure is used, calculate the concentra- tion in the sample using the response factor (RF) determined in Section 7.3.2 and Equa- tion 3.

As Is 

## Concentration (g/L) 

Ais RFVo 

Equation   3

where:

As  = Response for the parameter to be meas- ured.

Ais = Response for the internal standard.

Is   =  Amount  of  internal  standard  added  to each extract (g).

Vo = Volume of water extracted (L).

  - Determine the concentration of indi- vidual compounds in the sample analyzed by derivatization and  ECDGC  according to Equation 4.

AVt BD

## Concentration (g/L) 

Vi Vs CE

A = Mass of underivatized phenol represented by area of peak in sample chromatogram, determined from calibration curve in Section 7.5.3 (ng).

Vi = Volume of eluate injected (L).

Vt = Total volume of column eluate or com- bined fractions from which Vi was taken (L).

Vs  =  Volume  of  water  extracted  in  Section

10.10 (mL).

B = Total volume of hexane added in Section

12.5 (mL).

C = Volume of hexane sample solution added to cleanup column in Section 12.7 (mL).

D = Total volume of 2-propanol extract prior to derivatization (mL).

E = Volume of 2-propanol extract carried through derivatization in Section 12.1 (mL).

  - Report results in g/L without correc- tion for recovery data. All QC data obtained should be reported with the sample results.

- Method Performance

  - The method detection limit (MDL) is defined as the minimum concentration of a substance that can be measured and reported with 99% confidence that the value is above zero. 1 The MDL  concentrations listed  in Ta- bles 1 and 2 were obtained using reagent water. 12 Similar results were achieved using representative wastewaters. The MDL actu- ally achieved in a given analysis will vary depending on instrument sensitivity and ma- trix  effects.

  - This method was tested by 20 labora- tories using reagent water, drinking water, surface water, and three industrial wastewaters spiked as six concentrations over the range 12 to 450 g/L. 13 Single oper- ator precision, overall precision, and method accuracy were found to be directly related to the concentration of the parameter and es- sentially independent of the sample matrix. Linear equations to describe these relation- ships for a flame ionization detector are pre- sented in Table 4.

References

- 40 CFR part 136, appendix B.

- ‘‘Determination of Phenols in Industrial and Municipal Wastewaters,’’ EPA 600/4–84– ABC, National  Technical  Information  Serv- ice, PBXYZ, Springfield, Virginia 22161, No- vember 1984.

- Kawahara, F. K. ‘‘Microdetermination of Derivatives of Phenols and Mercaptans by Means of Electron Capture Gas Chroma- tography,’’ Analytical Chemistry, 40, 1009 (1968).

- ASTM Annual Book of Standards, Part 31, D3694–78. ‘‘Standard Practices for Prepa- ration of Sample Containers and for Preser- vation   of   Organic   Constituents,’’   American

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 604

Society for Testing and Materials, Philadel- phia.

- ‘‘Carcinogens—Working With Carcino- gens,’’ Department of Health, Education, and Welfare, Public Health Service, Center for Disease Control, National Institute for Occu- pational Safety and Health, Publication No. 77–206, August 1977.

- ‘‘OSHA Safety and Health Standards, General Industry,’’ (29 CFR part 1910), Occu- pational Safety and Health Administration, OSHA 2206 (Revised, January 1976).

- ‘‘Safety in Academic Chemistry Labora- tories,’’ American Chemical Society Publica- tion, Committee on Chemical Safety, 3rd Edition, 1979.

- Provost,  L.  P.,  and  Elder,  R.  S.  ‘‘Inter- pretation  of  Percent  Recovery  Data,’’  Amer- ican Laboratory, 15, 58–63 (1983). (The value

2.44 used in the equation in Section 8.3.3 is two times the value 1.22 derived in this re- port.)

- ASTM Annual Book of Standards, Part 31, D3370–76. ‘‘Standard Practices for Sam- pling Water,’’ American Society for Testing and  Materials,  Philadelphia.

- ‘‘Methods 330.4 (Titrimetric, DPD-FAS) and 330.5 (Spectrophotometric, DPD) for Chlorine, Total Residual,’’ Methmds for Chemical Analysis of Water and Wastes, EPA–600/4–79–020, U.S. Environmental Pro- tection Agency, Environmental Monitoring and Support Laboratory, Cincinnati, Ohio 45268, March 1979.

- Burke, J. A. ‘‘Gas Chromatography for Pesticide Residue Analysis; Some Practical Aspects,’’ Journal of the Association of Official Analytical Chemists, 48, 1037 (1965).

- ‘‘Development of Detection Limits, EPA Method 604, Phenols,’’ Special letter re- port for EPA Contract 68–03–2625, U.S. Envi- ronmental Protection Agency, Environ- mental Monitoring and Support Laboratory, Cincinnati, Ohio 45268.

- ‘‘EPA Method Study 14  Method 604-Phe- nols,’’ EPA 600/4–84–044, National Technical Information Service, PB84–196211, Spring- field, Virginia 22161, May 1984.

TABLE 1—CHROMATOGRAPHIC CONDITIONS AND

METHOD DETECTION LIMITS

| Parameter | Retention time (min) | Method de- tection limit (g/L) |
| --- | --- | --- |
| 2-Chlorophenol .......................... | 1.70 | 0.31 |
| 2-Nitrophenol ............................. | 2.00 | 0.45 |
| Phenol ....................................... | 3.01 | 0.14 |
| 2,4-Dimethylphenol .................... | 4.03 | 0.32 |
| 2,4-Dichlorophenol ..................... | 4.30 | 0.39 |
| 2,4,6-Trichlorophenol ................. | 6.05 | 0.64 |
| 4-Chloro-3-methylphenol ........... | 7.50 | 0.36 |
| 2,4-Dinitrophenol ....................... | 10.00 | 13.0 |
| 2-Methyl-4,6-dinitrophenol ......... | 10.24 | 16.0 |
| Pentachlorophenol ..................... | 12.42 | 7.4 |
| 4-Nitrophenol ............................. | 24.25 | 2.8 |

Column conditions: Supelcoport (80/100 mesh) coated with 1% SP–1240DA packed in a 1.8 m long 2 mm ID glass col- umn with nitrogen carrier gas at 30 mL/min flow rate. Column temperature was 80 C at injection, programmed immediately at 8 C/min  to 150  C final temperature. MDL were deter- mined with an FID.

TABLE 2—SILICA GEL FRACTIONATION AND ELECTRON CAPTURE GAS CHROMATOGRAPHY OF PFBB DERIVATIVES

| Parent compound | Percent recovery by frac- tion a | Retention time (min) | Method detection limit (g/L) |
| --- | --- | --- | --- |
|  | 1 | 2 | 3 | 4 |  |  |
| 2-Chlorophenol ............................................................................................ | ........ | 90 | 1 | ........ | 3.3 | 0.58 |
| 2-Nitrophenol ............................................................................................... | ........ | ........ | 9 | 90 | 9.1 | 0.77 |
| Phenol ......................................................................................................... | ........ | 90 | 10 | ........ | 1.8 | 2.2 |
| 2,4-Dimethylphenol ..................................................................................... | ........ | 95 | 7 | ........ | 2.9 | 0.63 |
| 2,4-Dichlorophenol ...................................................................................... | ........ | 95 | 1 | ........ | 5.8 | 0.68 |
| 2,4,6-Trichlorophenol .................................................................................. | 50 | 50 | ........ | ........ | 7.0 | 0.58 |
| 4-Chloro-3-methylphenol ............................................................................. | ........ | 84 | 14 | ........ | 4.8 | 1.8 |
| Pentachlorophenol ...................................................................................... | 75 | 20 | ........ | ........ | 28.8 | 0.59 |
| 4-Nitrophenol ............................................................................................... | ........ | ........ | 1 | 90 | 14.0 | 0.70 |

Column conditions: Chromosorb W-AW-DMCS (80/100 mesh) coated with 5% OV–17 packed in a 1.8 m long 2.0 mm ID glass column with 5% methane/95% argon carrier gas at 30 mL/min flow rate. Column temperature held isothermal at 200 C. MDL were determined with an ECD.

a Eluant composition:

Fraction 1—15% toluene in hexane. Fraction 2—40% toluene in hexane. Fraction 3—75% toluene in hexane. Fraction 4—15% 2-propanol in toluene.

#### Pt. 136, App. A, Meth. 604

40 CFR Ch. I (7–1–17 Edition)

TABLE 3—QC ACCEPTANCE CRITERIA—METHOD 604

| Parameter | Test conc. (g/L) | Limit for s (g/L) | Range for X¯ (g/L) | Range for P, Ps (per- cent) |
| --- | --- | --- | --- | --- |
| 4-Chloro-3-methylphenol ..................................................................................... | 100 | 16.6 | 56.7–113.4 | 49–122 |
| 2-Chlorophenol .................................................................................................... | 100 | 27.0 | 54.1–110.2 | 38–126 |
| 2,4-Dichlorophenol .............................................................................................. | 100 | 25.1 | 59.7–103.3 | 44–119 |
| 2,4-Dimethylphenol ............................................................................................. | 100 | 33.3 | 50.4–100.0 | 24–118 |
| 4,6-Dinitro-2-methylphenol .................................................................................. | 100 | 25.0 | 42.4–123.6 | 30–136 |
| 2,4-Dinitrophenol ................................................................................................. | 100 | 36.0 | 31.7–125.1 | 12–145 |
| 2-Nitrophenol ....................................................................................................... | 100 | 22.5 | 56.6–103.8 | 43–117 |
| 4-Nitrophenol ....................................................................................................... | 100 | 19.0 | 22.7–100.0 | 13–110 |
| Pentachlorophenol .............................................................................................. | 100 | 32.4 | 56.7–113.5 | 36–134 |
| Phenol ................................................................................................................. | 100 | 14.1 | 32.4–100.0 | 23–108 |
| 2,4,6-Trichlorophenol .......................................................................................... | 100 | 16.6 | 60.8–110.4 | 53–119 |

s—Standard deviation of four recovery measurements, in g/L (Section 8.2.4). X¯ —Average recovery for four recovery measurements, in g/L (Section 8.2.4).

P, Ps—Percent recovery measured (Section 8.3.2, Section 8.4.2).

NOTE: These criteria are based directly upon the method performance data in Table 4. Where necessary, the limits for recov- ery have been broadened to assure applicability of the limits to concentrations below those used to develop Table 4.

TABLE 4—METHOD ACCURACY AND PRECISION AS FUNCTIONS OF CONCENTRATION—METHOD 604

| Parameter | Accuracy, as re- covery, X(g/L) | Single Analyst precision, sr(g/ L) | Overall precision, S(g/L) |
| --- | --- | --- | --- |
| 4-Chloro-3-methylphenol ................................................................. 2-Chlorophenol ................................................................................ 2,4-Dichlorophenol .......................................................................... 2,4-Dimethylphenol .......................................................................... 4,6-Dinitro-2-methylphenol .............................................................. 2,4-Dinitrophenol ............................................................................. 2-Nitrophenol ................................................................................... 4-Nitrophenol ................................................................................... Pentachlorophenol ........................................................................... Phenol ............................................................................................. 2,4,6-Trichlorophenol ....................................................................... | 0.87C–1.97 0.83C–0.84 0.81C + 0.48 0.62C–1.64 0.84C–1.01 0.80C–1.58 0.81C–0.76 0.46C + 0.18 0.83C + 2.07 0.43C + 0.11 0.86C–0.40 | 0.11X¯ –0.21 0.18X¯ + 0.20 0.17X¯ –0.02 0.30X¯ –0.89 0.15X¯ + 1.25 0.27X¯ –1.15 0.15X¯ + 0.44 0.17X¯ + 2.43 0.22X¯ –0.58 0.20X¯ –0.88 0.10X¯ + 0.53 | 0.16X¯ + 1.41 0.21X¯ + 0.75 0.18X¯ + 0.62 0.25X¯ + 0.48 0.19X¯ + 5.85 0.29X¯ + 4.51 0.14X¯ + 3.84 0.19X¯ + 4.79 0.23X¯ + 0.57 0.17X¯ + 0.77 0.13X¯ + 2.40 |

X= Expected recovery for one or more measurements of a sample containing a concentration of C, in g/L.

sr= Expected single analyst standard deviation of measurements at an average concentration found of X¯ , in g/L. S= Expected interlaboratory standard deviation of measurements at an average concentration found of X¯ , in g/L. C = True value for the concentration, in g/L.

X¯ = Average recovery found for measurements of samples containing a concentration of C, in g/L.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 604

Pt. 136, App. A, Meth. 605

40 CFR Ch. I (7–1–17 Edition)

METHOD  605—BENZIDINES

- Scope and Application

  - This method covers the determination of certain benzidines. The following param- eters can be determined by this method:

| Parameter | Storet No | CAS No. |
| --- | --- | --- |
| Benzidine ................................... 3,3-Dichlorobenzidine ............... | 39120 34631 | 92–87–5 91–94–1 |

  - This is a high performance liquid chro- matography (HPLC) method applicable to the determination of the compounds listed above in municipal and industrial discharges

as provided under 40 CFR 136.1. When this method is  used  to  analyze  unfamiliar  sam- ples for the compounds above, identifications should be supported by  at  least  one  addi- tional qualitative technique. This method describes electrochemical conditions at a second potential which can be used to con- firm measurements made with this method. Method 625 provides gas chromatograph/mass spectrometer (GC/MS) conditions  appro- priate for the qualitative and quantitative confirmation of results for the parameters listed above, using the extract produced by this   method.

  - The  method  detection  limit  (MDL,  de- fined in Section 14.1) 1  for each parameter is

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 605

listed in Table 1. The MDL for a specific wastewater may differ from those listed, de- pending upon the nature of the interferences in the sample matrix.

  - Any modification of this method,  be- yond those expressly permitted, shall be con- sidered as a major modification subject to application and approval of alternate test procedures under 40 CFR 136.4 and 136.5.

  - This method is restricted to use by or under the supervision of analysts experi- enced in the use of HPLC instrumentation and in the interpretation of liquid chromatograms. Each  analyst must  dem- onstrate the ability to generate acceptable results with this method using the procedure described in Section 8.2.

- Summary of Method

  - A measured volume of sample, ap- proximately 1–L, is extracted with chloro- form using liquid-liquid extractions in a separatory funnel. The chloroform extract is extracted with acid. The acid extract is then neutralized and extracted with chloroform. The final chloroform extract is exchanged to methanol while being concentrated using a rotary evaporator. The extract is mixed with buffer and separated by HPLC. The benzidine compounds are measured with an electro- chemical detector. 2

  - The acid back-extraction acts as a general purpose cleanup to aid in the elimi- nation of interferences.

- Interferences

  - Method interferences may be caused by contaminants in solvents, reagents, glass- ware, and other sample processing hardware that lead to discrete artifacts and/or ele- vated baselines in chromatograms. All of these materials must be routinely dem- onstrated to be free from interferences under the conditions of the analysis by running laboratory reagent blanks as described in Section 8.1.3.

    - Glassware must be scrupulously cleaned. 3 Clean all glassware as soon as pos- sible after use by rinsing with the last  sol- vent used in it. Solvent rinsing should be fol- lowed by detergent washing with hot water, and rinses with tap water and distilled water. The glassware should then be drained dry, and heated in a muffle furnace at 400 C for 15 to 30 min. Some thermally stable ma- terials may not be eliminated by this treat- ment. Solvent rinses with acetone and pes- ticide quality hexane may be substituted for the muffle furnace heating. Volumetric ware should not be heated in a muffle furnace. After drying and cooling, glassware  should be sealed and stored in a clean environment to prevent any accumulation of dust or other contaminants. Store inverted or capped with aluminum  foil.

    - The use of high purity reagents and solvents helps to minimize interference prob- lems. Purification of solvents  by  distillation in all-glass systems may be required.

  - Matrix interferences may be caused by contaminants that are co-extracted from the sample. The extent of matrix interferences will vary considerably from source to source, depending upon the nature and diversity of the industrial complex or municipality being sampled. The cleanup procedures that are in- herent in the extraction step are used to overcome many of these interferences, but unique samples may require additional cleanup approaches to achieve the MDL list- ed in Table 1.

  - Some dye plant effluents contain large amounts of components with retention times closed to benzidine. In these cases, it has been found useful to reduce the electrode po- tential in  order  to  eliminate  interferences and still detect benzidine. (See Section 12.7.)

- Safety

  - The toxicity or carcinogenicity of each reagent used in this method has not been precisely defined; however, each chem- ical compound should be treated as a poten- tial health harzard. From this viewpoint, ex- posure to these chemicals must be reduced to the lowest possible level by whatever means available. The laboratory is responsible for maintaining a current awareness file of OSHA regulations regarding the safe han- dling of the chemicals specified in this meth- od. A reference file of material data handling sheets should also be made available to all personnel involved in the chemical analysis. Additional references to laboratory safety are available and have been identified 4 6 for the information of the analyst.

  - The following parameters covered by this method have been  tentatively  classified as known or suspected, human or mamma- lian carcinogens:  benzidine and  3,3- dichlorobenzidine. Primary  standards  of these toxic compounds should be prepared in a hood. A NIOSH/MESA approved toxic gas respirator should be worn when the analyst handles high concentrations of these toxic compounds.

  - Exposure to chloroform should be minimized by performing all extractions and extract concentrations in a hood or other well-ventiliated area.

- Apparatus and Materials

  - Sampling equipment, for discrete or composite  sampling.

    - Grab sample bottle—1–L or 1-qt, amber glass, fitted with a screw cap lined with Teflon. Foil may be substituted for Tef- lon if the sample is not corrosive. If amber bottles are not available, protect samples from light. The bottle and cap liner must be washed, rinsed  with acetone or methylene

#### Pt. 136, App. A, Meth. 605

chloride, and dried before use to minimize contamination.

    - Automatic sampler (optional)—The sampler must incorporate glass sample con- tainers for the collection of a minimum of 250 mL of sample. Sample containers must be kept refrigerated at 4 C and protected from light during compositing. If the sampler uses a peristaltic pump, a minimum length of compressible silicone rubber tubing may be used. Before use, however, the compressible tubing should be thoroughly rinsed with methanol, followed by repeated rinsings with distilled water to minimize the potential for contamination of the sample. An integrating flow meter is required to collect flow propor- tional  composites.

  - Glassware (All specifications are sug- gested):

    - Separatory funnels—2000, 1000, and 250-mL,  with  Teflon  stopcock.

    - Vials—10 to 15-mL, amber glass, with Teflon-lined screw cap.

    - Rotary evaporator.

    - Flasks—Round bottom, 100–mL, with 24/40 joints.

    - Centrifuge tubes—Conical, grad- uated, with Teflon-lined screw caps.

    - Pipettes—Pasteur, with bulbs.

  - Balance—Analytical, capable of accu- rately weighing 0.0001 g.

  - High performance liquid chro- matograph (HPLC)—An analytical system complete with column supplies, high pres- sure syringes, detector, and compatible re- corder. A data system is recommended for measuring peak areas and retention times.

    - Solvent delivery system—With pulse damper, Altex 110A or equivalent.

    - Injection valve (optional)—Waters U6K or equivalent.

    - Electrochemical	detector—Bio- analytical Systems LC–2A with glassy car- bon electrode, or equivalent. This detector has proven effective in the analysis of wastewaters for the parameters listed in the scope (Section 1.1), and was used to develop the method performance statements in Sec- tion 14. Guidelines for the use of alternate detectors are provided in Section 12.1.

    - Electrode polishing kit—Princeton Applied Research Model 9320 or equivalent.

    - Column—Lichrosorb RP–2, 5 micron particle diameter, in a 25 cm 4.6 mm ID stainless steel column. This  column  was  used to develop the method performance state- ments in Section 14. Guidelines for the use of alternate column packings are provided in Section 12.1.

- Reagents

  - Reagent water—Reagent water is de- fined as a water in which an  interferent  is not observed at the  MDL  of  the  parameters of  interest.

#### 40 CFR Ch. I (7–1–17 Edition)

  - Sodium hydroxide solution (5 N)—Dis- solve 20 g of NaOH (ACS) in  reagent  water and dilute to 100 mL.

  - Sodium hydroxide solution (1 M)—Dis- solve 40 g of NaOH (ACS) in  reagent  water and dilute to 1 L.

  - Sodium thiosulfate—(ACS) Granular.

  - Sodium tribasic phosphate (0.4 M)— Dissolve 160 g of trisodium phosphate deca- hydrate (ACS) in reagent water and dilute to 1 L.

  - Sulfuric acid (1 + 1)—Slowly, add  50 mL of  H2SO4 (ACS, sp.  gr.  1.84) to  50  mL of reagent water.

  - Sulfuric acid (1 M)—Slowly, add 58 mL of H2SO4 (ACS, sp. gr. 1.84) to reagent water and dilute to 1 L.

  - Acetate buffer (0.1 M, pH 4.7)—Dissolve

5.8 mL of glacial acetic acid (ACS) and 13.6 g of sodium acetate trihydrate (ACS) in rea- gent water which has been purified by filtra- tion through a RO–4 Millipore System or equivalent and dilute to 1 L.

  - Acetonitrile, chloroform (preserved with 1% ethanol), methanol—Pesticide qual- ity  or  equivalent.

  - Mobile phase—Place equal volumes of filtered acetonitrile (Millipore type  FH  filter or equivalent) and filtered acetate buffer (Millipore type GS filter or equivalent) in a narrow-mouth, glass container and mix thor- oughly. Prepare fresh weekly. Degas daily by sonicating under vacuum, by heating and stirring, or by purging with helium.

  - Stock    standard    solutions    (1.00    g/

L)—Stock standard solutions may be pre- pared from pure standard materials or pur- chased as certified solutions.

    - Prepare stock standard solutions by accurately weighing about 0.0100 g of pure material. Dissolve  the  material  in  methanol and dilute to volume in a 10–mL volumetric flask. Larger volumes can be used at the con- venience of the analyst. When compound pu- rity is assayed to be  96%  or  greater,  the weight can be used without correction to cal- culate the concentration of the stock stand- ard. Commercially  prepared  stock  standards can be used at any concentration if they are certified by the manufacturer or by an inde- pendent  source.

    - Transfer the stock standard solu- tions into Teflon-sealed screw-cap bottles. Store at 4 C and protect from light. Stock standard solutions should be checked fre- quently for signs of degradation or evapo- ration, especially just prior to preparing calibration standards from them.

    - Stock standard solutions must be replaced after six months, or sooner if com- parison with check standards indicates a problem.

6.12 Quality control check sample con- centrate—See Section 8.2.1.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 605

- Calibration

  - Establish chromatographic operating conditions equivalent to those given in Table

- The HPLC system can be calibrated  using the external standard technique (Section 7.2) or the internal standard technique (Section 7.3).

  - External standard calibration proce- dure:

    - Prepare calibration standards at a minimum of three concentration levels  for each parameter of interest by adding vol- umes of one or more stock standards to a volumetric flask and diluting to volume with mobile phase. One of the external standards should be at a concentration near, but above, the MDL (Table 1) and the other concentra- tions should correspond to the expected range of concentrations found in real sam- ples or should define the working range of the detector.

    - Using syringe injections of 5 to 25 L

or a constant volume injection loop, analyze each calibration standard according to Sec- tion 12 and tabulate peak height or area re- sponses against  the mass injected. The re- sults can be used to prepare a calibration curve for each compound. Alternatively, if the ratio of response to amount injected (calibration factor) is a constant over the working range (<10% relative standard devi- ation, RSD), linearity through the origin can be assumed and the average ratio or calibra- tion factor can be used in place of a calibra- tion curve.

  - Internal standard calibration proce- dure—To use this approach, the analyst must select one or more internal standards that are similar in analytical behavior to the compounds of interest. The analyst must fur- ther demonstrate that the measurement of the internal standard is not affected by method or matrix interferences. Because of these limitations, no internal standard  can be suggested that is applicable to all sam- ples.

    - Prepare calibration standards at a minimum of three concentration levels  for each parameter of interest by adding vol- umes of one or more stock standards to a volumetric flask. To each calibration stand- ard, add a known constant amount of one or more internal standards, and dilute to vol- ume with mobile phase. One of the standards should be at a concentration near, but above, the MDL and the other concentrations should correspond to the expected range of concentrations found in real samples or should define the working range of the detec- tor.

    - Using syringe injections of 5 to 25 L

or a constant volume injection loop, analyze each calibration standard according to Sec- tion 12 and tabulate peak height or area re- sponses against concentration for each com- pound  and  internal  standard.  Calculate  re-

sponse factors (RF) for each compound using Equation 1.

RF = (As)(Cis (Ais)(Cs)

Equation   1

where:

As  = Response for the parameter to be meas- ured.

Ais = Response for the internal standard.

Cis  = Concentration of the internal standard (g/L).

Cs   =  Concentration  of  the  parameter  to  be measured (g/L).

If the RF value over the working range is a constant (<10% RSD), the RF can be as- sumed to be invariant and the average RF can be used for calculations. Alternatively, the results can be used to plot a calibration curve of response ratios, As/Ais, vs. RF.

  - The working calibration curve, cali- bration factor, or RF must be verified on each working day by the measurement of one or more calibration standards. If the re- sponse for any parameter varies from the predicted response by more than 15%, a new calibration curve must be prepared for that compound. If serious loss of response occurs, polish the electrode and recalibrate.

  - Before using any cleanup procedure, the analyst must process a series of calibra- tion standards through the procedure to vali- date elution patterns and the absence of interferences from the reagents.

  - Quality Control

  - Each laboratory that uses this method is required to operate a formal quality  con- trol program. The minimum requirements of this program consist of an initial demonstra- tion of laboratory capability and an ongoing analysis of spiked samples to evaluate and document data quality. The laboratory must maintain records to document the quality of data that is generated. Ongoing data quality checks are compared with established per- formance criteria to determine if the results of analyses meet the performance character- istics of the method. When results of sample spikes indicate atypical method perform- ance, a quality control check  standard  must be analyzed to confirm that the measure- ments were performed in an in-control mode of operation.

    - The analyst must make an initial, one-time, demonstration of the ability to generate acceptable accuracy and precision with this method. This  ability  is  established as described in Section 8.2.

    - In recognition of advances that are occurring in chromatography, the analyst is permitted certain options (detailed in Sec- tions 10.9, 11.1, and 12.1) to improve the sepa- rations or lower the cost of measurements. Each time such a modification is  made  to the method, the analyst is required to repeat the procedure in Section 8.2.

#### Pt. 136, App. A, Meth. 605

    - Before processing any samples, the analyst must analyze a  reagent  water  blank to demonstrate that interferences from the analytical system and glassware are under control. Each time a set of samples is ex- tracted or reagents are changed, a reagent water blank must be processed as a safe- guard  against  laboratory  contamination.

    - The laboratory must, on an ongoing basis, spike and analyze a minimum of 10% of all samples to monitor and evaluate lab- oratory data quality. This procedure is de- scribed in Section 8.3.

    - The laboratory must, on an ongoing basis, demonstrate through the analyses of quality control  check standards  that  the op- eration of the measurement system is in con- trol.  This  procedure  is  described  in  Section

8.4. The frequency of the check standard analyses is equivalent to 10% of all samples analyzed but may be reduced if spike recov- eries from samples (Section 8.3) meet all specified quality control criteria.

    - The laboratory must maintain per- formance records to document the quality of data that is generated. This procedure is de- scribed in Section 8.5.

  - To establish the ability to generate acceptable accuracy and precision, the ana- lyst must perform the following operations.

    - A quality control (QC) check sample concentrate is required containing benzidine and/or 3,3-dichlorobenzidine at a concentra- tion of 50 g/mL each in methanol. The QC check sample concentrate must be obtained from the U.S. Environmental Protection Agency, Environmental Monitoring and Sup- port Laboratory in Cincinnati, Ohio, if avail- able. If not available from  that  source,  the QC check sample concentrate must be ob- tained from another external source. If not available from either source above, the QC check sample concentrate must be prepared by the laboratory using stock standards pre- pared independently from those used for cali- bration.

    - Using a pipet, prepare QC check sam- ples at a concentration of 50 g/L by adding

1.00 mL of QC check sample concentrate to each of four 1–L-L aliquots of reagent water.

    - Analyze the well-mixed QC check samples according to the  method  beginning in Section 10.

    - Calculate the average recovery (X¯ ) in

g/L, and the standard deviation of the re- covery (s) in g/L, for each parameter using the four results.

    - For each parameter compare s and X¯

with the corresponding acceptance criteria for   precision   and   accuracy,   respectively,

found in Table 2. If s and X¯  for all param-

eters of interest meet the acceptance cri- teria, the system performance is acceptable and analysis of actual samples can begin. If any individual s exceeds the precision limit

or any individual X¯  falls outside the range

for accuracy, the system performance is un-

#### 40 CFR Ch. I (7–1–17 Edition)

acceptable for that parameter. Locate and correct the source of the problem and repeat the test for all parameters of interest begin- ning with Section 8.2.2.

  - The laboratory must, on an ongoing basis, spike at least 10% of the samples from each sample site being monitored to assess accuracy. For laboratories analyzing one to ten samples per month, at least one spiked sample per month is required.

    - The concentration of the spike in the sample should be determined as follows:

      - If, as in compliance monitoring, the concentration of a specific parameter in the sample is being checked against a regu- latory concentration limit, the spike should be at that limit or 1 to 5 times higher than the background concentration determined in Section 8.3.2, whichever concentration would be larger.

      - If the concentration of a specific parameter in the sample  is  not  being checked against a limit specific to that pa- rameter, the spike should be at 50 g/L or 1 to 5  times  higher than  the  background  con- centration determined in Section 8.3.2, whichever concentration would be larger.

      - If it is impractical to determine background levels before spiking (e.g., max- imum holding times will be exceeded), the spike concentration should be (1) the regu- latory concentration limit, if any; or, if none

(2) the larger of either 5  times  higher  than the expected background concentration or 50

g/L.

    - Analyze one sample aliquot to deter- mine the background concentration (B) of each parameter. If necessary, prepare a new QC check sample concentrate (Section 8.2.1) appropriate for the background concentra- tions in the sample. Spike a second sample aliquot with 1.0 mL of the QC check sample concentrate and analyze it to determine the concentration after spiking (A) of each pa- rameter. Calculate each percent recovery (P) as 100(A¥B)%/T, where T is the known true value of the spike.

    - Compare the percent recovery (P) for each parameter with the corresponding QC acceptance criteria found in Table 2. These acceptance criteria were calculated to in- clude an allowance for error in measurement of both the background and spike concentra- tions, assuming a spike  to  background  ratio of 5:1. This error will be accounted for to the extent that the analyst’s spike to back- ground ratio approaches 5:1. 7 If spiking was performed at a concentration lower than 50

g/L, the analyst must use either the QC ac- ceptance criteria in Table 2, or optional QC acceptance  criteria  calculated  for  the  spe-

cific spike concentration. To calculate op- tional acceptance criteria for the recovery of a parameter: (1) Calculate accuracy (X) using the equation in Table 3, substituting

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 605

the spike concentration (T) for C; (2) cal- culate overall precision (S) using the equa- tion in Table 3, substituting Xfor X¯ ; (3) cal-

culate the range for recovery at the spike concentration as (100 X/T)2.44(100 S/T)%. 7

    - If any individual P falls outside the designated range for recovery, that param- eter has failed the acceptance criteria. A check standard containing each parameter that failed the criteria must be analyzed as described in Section 8.4.

  - If any parameter fails the acceptance criteria for recovery in Section 8.3, a QC check standard containing each parameter that failed must be prepared and analyzed.

NOTE: The frequency for the required anal- ysis of a QC check standard will depend upon the number of parameters being simulta- neously tested, the complexity of the sample matrix, and the performance of the labora- tory.

    - Prepare the QC check standard by adding 1.0 mL of QC check sample con- centrate (Sections 8.2.1 or 8.3.2) to 1 L of rea- gent water.  The  QC  check  standard  needs only to contain the parameters that failed criteria  in  the  test  in  Section  8.3.

    - Analyze the QC check standard to determine the concentration measured (A) of each parameter. Calculate each percent re- covery (Ps) as 100 (A/T)%, where T is the true value of the standard concentration.

    - Compare the percent recovery (Ps) for each parameter with the corresponding QC acceptance criteria found in Table 2. Only parameters that failed the test in Section 8.3 need to be compared with these  criteria.  If the recovery of any such parameter falls out- side the designated range, the laboratory performance for that parameter is judged to be out of control, and the problem must be immediately identified and corrected. The analytical result for that parameter in the unspiked sample is suspect  and may not  be reported for regulatory compliance purposes.

  - As part of the QC program for the lab- oratory, method accuracy for wastewater samples must be assessed and records must be maintained. After the analysis of five spiked wastewater samples as in Section 8.3,

calculate  the  average  percent  recovery  (P¯ )

and the standard deviation of the percent re- covery (sp). Express the accuracy assessment

as a percent recovery interval from P¯ ¥2sp to P¯ + 2sp. If P¯ = 90% and sp = 10%, for example,

the accuracy interval is expressed as 70– 110%. Update the accuracy  assessment  for each parameter on a regular basis (e.g. after each five to  ten  new  accuracy  measure- ments).

  - It is recommended that the laboratory adopt additional quality assurance practices for use with this method. The specific prac- tices that are most productive depend upon the needs of the laboratory and the nature of the  samples.  Field  duplicates  may  be  ana-

lyzed to assess the precision of the environ- mental measurements. When doubt exists over the identification of a peak on the chro- matogram, confirmatory techniques such as HPLC with a dissimilar column, gas chroma- tography, or mass spectrometer must  be used. Whenever possible, the laboratory should analyze standard reference materials and participate in relevant performance evaluation  studies.

  - Sample Collection, Preservation, and Handling

  - Grab samples must be collected  in glass containers. Conventional sampling practices 8 should be followed, except  that the bottle must not be prerinsed with sample before collection. Composite samples should be collected in refrigerated  glass  containers in accordance with the requirements of the program. Automatic sampling equipment must be as free as possible of Tygon tubing and other potential sources of contamina- tion.

  - All samples must be iced or refrig- erated at 4 C and stored  in  the  dark  from the time of collection until extraction. Both benzidine and 3,3-dichlorobenzidine are eas- ily oxidized. Fill the sample bottles and, if residual chlorine is present, add 80 mg of so- dium thiosulfate per liter of sample and mix well. EPA Methods 330.4 and 330.5 may be used for  measurement of  residual chlorine. 9 Field test kits are available for this purpose. After mixing, adjust the pH of the sample to a range of 2 to 7 with sulfuric acid.

  - If 1,2-diphenylhydrazine is likely to be present,  adjust  the  pH  of  the  sample  to  4.0

0.2 to prevent rearrangement to benzidine.

  - All samples must be extracted within 7 days of collection. Extracts  may  be  held  up to 7 days before analysis, if stored under an inert (oxidant free) atmosphere. 2  The  ex- tract should be protected from light.

  - Sample Extraction

  - Mark the water meniscus on the side of the sample bottle for later determination of sample volume. Pour the entire sample into a 2–L separatory funnel. Check the pH of the sample with wide-range pH paper and adjust to within the range of 6.5 to 7.5 with sodium hydroxide solution or sulfuric acid.

  - Add 100 mL of chloroform to the sam- ple bottle,  seal,  and  shake  30  s  to  rinse  the inner surface. (Caution: Handle  chloroform in a well ventilated area.) Transfer the sol- vent to the separatory funnel and  extract the sample by shaking the funnel for 2 min with periodic venting to release excess pres- sure. Allow the organic  layer  to  separate from the water phase for a minimum of 10 min. If the emulsion interface between  lay- ers is more than one-third the volume of the solvent layer, the analyst must employ me- chanical  techniques  to  complete  the  phase

#### Pt. 136, App. A, Meth. 605

separation. The optimum technique depends upon the sample, but may include stirring, filtration of the emulsion through glass wool, centrifugation, or other physical meth- ods. Collect the chloroform extract in a 250- mL separatory funnel.

  - Add a 50-mL volume of chloroform to the sample bottle and repeat the extraction procedure a second time, combining the ex- tracts in the separatory funnel. Perform a third extraction in the same manner.

  - Separate and discard any aqueous layer remaining in the 250-mL separatory funnel after combining the organic extracts. Add 25  mL of  1 M  sulfuric  acid and  extract the sample by shaking the funnel for 2 min. Transfer the aqueous layer to a 250-mL beak- er. Extract with two additional 25-mL por- tions of 1 M sulfuric acid and combine  the acid extracts in the beaker.

  - Place a stirbar in the 250-mL beaker and stir the acid extract while carefully add- ing 5 mL of 0.4 M sodium tribasic phosphate. While monitoring with a pH meter,  neu- tralize the extract to a pH between 6 and 7 by dropwise addition of 5 N sodium hydroxide solution while stirring the solution vigor- ously. Approximately 25 to 30 mL of 5 N so- dium hydroxide solution will be required and it should be added over at least a 2-min pe- riod. Do not allow the sample pH to exceed 8.

  - Transfer the  neutralized  extract  into a 250-mL separatory funnel. Add 30 mL of chloroform and shake the funnel for 2 min. Allow the phases to separate, and  transfer the organic layer to a second 250-mL sepa- ratory  funnel.

  - Extract the aqueous layer with two additional 20-mL aliquots of chloroform as before. Combine the extracts in the 250-mL separatory  funnel.

  - Add 20 mL of reagent water to the combined organic layers and shake for 30 s.

  - Transfer the organic extract into a 100-mL round bottom flask. Add 20 mL of methanol and concentrate to 5 mL with a ro- tary evaporator at reduced pressure and 35

C. An aspirator is recommended for  use  as the source of vacuum. Chill the receiver with ice. This operation requires approximately 10 min. Other concentration techniques may be used if the requirements of Section 8.2 are met.

  - Using a 9-in. Pasteur pipette, trans- fer the extract to a 15-mL, conical, screw-cap centrifuge tube. Rinse the flask, including the entire side wall, with 2-mL portions of methanol and combine with the original ex- tract.

  - Carefully concentrate the extract to

0.5 mL using a  gentle  stream  of  nitrogen while heating in a 30 C water bath. Dilute to 2 mL with methanol, reconcentrate to 1  mL, and dilute to 5 mL with  acetate  buffer.  Mix the extract thoroughly.  Cap  the  centrifuge tube and store refrigerated  and  protected from  light  if  further  processing  will  not  be

#### 40 CFR Ch. I (7–1–17 Edition)

performed immediately. If the extract  will be stored longer than two days, it should be transferred to a Teflon-sealed screw-cap vial. If the sample extract requires no further cleanup, proceed with HPLC analysis (Sec- tion 12). If the sample requires further clean- up, proceed to Section 11.

  - Determine the original sample vol- ume by refilling the sample bottle to the mark and transferring the liquid to a 1,000- mL graduated cylinder. Record the sample volume to the nearest 5 mL.

  - Cleanup and Separation

11.1 Cleanup procedures may not be nec- essary for a relatively clean sample matrix. If particular circumstances demand the use of a cleanup procedure, the analyst first must demonstrate that the requirements of Section 8.2 can be met using the method as revised to incorporate the cleanup proce- dure.

  - High Performance Liquid Chromatography

12.1 Table 1 summarizes the recommended operating conditions for the  HPLC.  Included in this table are retention times, capacity factors, and MDL that can be achieved under these conditions. An example of the separa- tions achieved by this HPLC column is shown in Figure 1. Other HPLC columns, chromatographic conditions,  or  detectors may  be  used  if  the  requirements  of  Section

8.2 are met. When the HPLC is idle, it is ad- visable to maintain a 0.1 mL/min flow through the column to prolong column life.

  - Calibrate the system daily as de- scribed in Section 7.

  - If the internal standard calibration procedure is being used, the internal stand- ard must be added to the sample extract and mixed thoroughly immediately before injec- tion into the instrument.

  - Inject 5 to 25 L of the sample extract

or standard into the HPLC. If constant vol- ume injection loops are not used, record the volume injected  to  the nearest  0.05  L,  and the resulting peak size in  area  or  peak height  units.

  - Identify the parameters in the sample by comparing the retention times of the peaks in the sample chromatogram with those of the peaks in standard chromatograms. The width of the retention time window used to make identifications should be based upon measurements of ac- tual retention time variations of standards over the course of a day. Three times the standard deviation of a retention time for a compound can be used to calculate a sug- gested window size; however, the experience of the analyst should weigh heavily in the interpretation of chromatograms.

  - If the response for a peak exceeds the working range of the system, dilute the ex- tract with mobile phase and reanalyze.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 605

  - If the measurement of the peak re- sponse for benzidine is prevented by the pres- ence of interferences, reduce the electrode potential to + 0.6 V and reanalyze. If the ben- zidine peak is still obscured by interferences, further cleanup is required.

  - Calculations

  - Determine the concentration of indi- vidual compounds in the sample.

    - If the external standard calibration procedure is used, calculate the amount of material injected from the peak response using the calibration curve or calibration factor determined in Section 7.2.2. The con- centration in the sample can be calculated from Equation 2.

AVt 

## Concentration (g/L) 

Vi Vs 

Equation   2

where:

A = Amount of material injected (ng). Vi = Volume of extract injected (L). Vt = Volume of total extract (L).

Vs = Volume of water extracted (mL).

    - If the internal standard calibration procedure is used, calculate the concentra- tion in the sample using the response factor (RF) determined in Section 7.3.2 and Equa- tion 3.

As Is 

## Concentration (g/L) 

Ais RFVo 

Equation   3

where:

As  = Response for the parameter to be meas- ured.

Ais = Response for the internal standard.

Is   =  Amount  of  internal  standard  added  to each extract (g).

Vo = Volume of water extracted (L).

13.2 Report results in g/L without correc- tion for recovery data. All QC data obtained should be reported with the sample results.

  - Method Performance

  - The method detection limit (MDL) is defined as the minimum concentration of a substance that can be measured and reported with 99% confidence that the value is above zero. 1 The MDL concentrations listed  in Table 1 were obtained using reagent water. 10 Similar results were achieved using rep- resentative wastewaters. The MDL actually achieved in a given analysis will vary de- pending on instrument sensitivity and ma- trix  effects.

  - This method has been tested for lin- earity of spike recovery from reagent water and has been demonstrated to be applicable

over the concentration range from 7 MDL to 3000 MDL. 10

  - This method was tested by 17 labora- tories using reagent water, drinking water, surface water, and three industrial wastewaters spiked at six concentrations over the range 1.0 to 70 g/L. 11 Single oper- ator precision, overall precision, and method accuracy were found to be directly related to the concentration of the parameter and es- sentially independent of the sample matrix. Linear equations to describe these relation- ships are presented in Table 3.

References

- 40 CFR part 136, appendix B.

- ‘‘Determination of Benzidines in  Indus- trial and Muncipal Wastewaters,’’ EPA  600/4– 82–022, National Technical Information Serv- ice, PB82–196320, Springfield, Virginia 22161, April 1982.

- ASTM Annual Book of Standards, Part 31, D3694–78. ‘‘Standard Practices for Prepa- ration of Sample Containers and for Preser- vation of Organic Constituents,’’ American Society for Testing and Materials, Philadel- phia.

- ‘‘Carcinogens—Working With Carcino- gens,’’ Department of Health, Education, and Welfare, Public Health Service, Center for Disease Control, National Institute for Occu- pational Safety and Health, Publication No. 77–206, August 1977.

- ‘‘OSHA Safety and Health Standards, General Industry,’’ (29 CFR part 1910), Occu- pational Safety and Health Administration, OSHA 2206 (Revised, January 1976).

- ‘‘Safety in Academic Chemistry Labora- tories,’’ American Chemical Society Publica- tion, Committee on Chemical Safety, 3rd Edition, 1979.

- Provost, L.P., and Elder, R.S. ‘‘Interpre- tation of Percent Recovery Data,’’ American Laboratory, 15, 58–63 (1983). (The value 2.44 used in the equation in Section 8.3.3 is two times the value 1.22 derived in this report.)

- ASTM Annual Book of Standards, Part 31, D3370–76. ‘‘Standard Practices for Sam- pling Water,’’ American Society for Testing and  Materials,  Philadelphia.

- ‘‘Methods 330.4 (Titrimetric, DPD-FAS) and 330.5 (Spectrophotometric, DPD) for Chlorine Total Residual,’’ Methods for Chemical Analysis of Water and Wastes, EPA–600/4–79–020, U.S. Environmental Pro- tection Agency, Environmental Monitoring and Support Laboratory, Cincinnati, Ohio 45268, March 1979.

- ‘‘EPA Method Study 15, Method 605 (Benzidines),’’ EPA 600/4–84–062, National Technical Information Service, PB84–211176, Springfield, Virginia 22161, June 1984.

- ‘‘EPA Method Validation Study 15, Method 605 (Benzidines),’’ Report for EPA Contract 68–03–2624 (In preparation).

#### Pt. 136, App. A, Meth. 605

40 CFR Ch. I (7–1–17 Edition)

TABLE 1—CHROMATOGRAPHIC CONDITIONS AND METHOD DETECTION LIMITS

| Parameter | Retention time (min) | Column ca- pacity factor (k) | Method de- tection limit (g/L) |
| --- | --- | --- | --- |
| Benzidine ....................................................................................................................... 3,3-Dichlorobenzidine ................................................................................................... | 6.1 12.1 | 1.44 3.84 | 0.08 0.13 |

HPLC Column conditions: Lichrosorb RP–2, 5 micron particle size, in a 25 cm 4.6 mm ID stainless steel column. Mobile Phase: 0.8 mL/min of 50% acetonitrile/50% 0.1M pH 4.7 acetate buffer. The MDL were determined using an electrochemical de- tector operated at + 0.8 V.

TABLE 2—QC ACCEPTANCE CRITERIA—METHOD 605

| Parameter | Test conc. (g/ L) | Limit for s (g/L) | Range for X¯ (g/L) | Range for P, Ps (percent) |
| --- | --- | --- | --- | --- |
| Benzidine ............................................................................................................. 3.3-Dichlorobenzidine ......................................................................................... | 50 50 | 18.7 23.6 | 9.1–61.0 18.7–50.0 | D–140 5–128 |

s = Standard deviation of four recovery measurements, in g/L (Section 8.2.4). X¯ = Average recovery for four recovery measurements, in g/L (Section 8.2.4).

P, Ps  = Percent recovery measured (Section 8.3.2, Section 8.4.2). D = Detected; result must be greater than zero.

Note: These criteria are based directly upon the method performance data in Table 3. Where necessary, the limits for recovery have been broadened to assure applicability of the limits to concentrations below those used to develop Table 3.

TABLE 3—METHOD ACCURACY AND PRECISION AS FUNCTIONS OF CONCENTRATION—METHOD 605

| Parameter | Accuracy, as recovery, X(g/L) | Single analyst precision, sr (g/L) | Overall preci- sion, S(g/L) |
| --- | --- | --- | --- |
| Benzidine ........................................................................................................... 3,3-Dichlorobenzidine ....................................................................................... | 0.70C + 0.06 0.66C + 0.23 | 0.28X¯ + 0.19 0.39X¯ ¥0.05 | 0.40X¯ + 0.18 0.38X¯ + 0.02 |

X= Expected recovery for one or more measurements of a sample containing a concentration of C, in g/L.

sr= Expected single analyst standard deviation of measurements at an average concentration found of X¯ , in g/L. S= Expected interlaboratory standard deviation of measurements at an average concentration found of X¯ , in g/L. C = True value for the concentration, in g/L.

X¯ = Average recovery found for measurements of samples containing a concentration of C, in g/L.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 605

Pt. 136, App. A, Meth. 606

METHOD 606—PHTHALATE ESTER

- Scope and Application

  - This method covers the determination of certain phthalate esters. The following pa- rameters can be determined by this method:

| Parameter | STORET No. | CAS No. |
| --- | --- | --- |
| Bis(2-ethylhexyl) phthalate ................ | 39100 | 117–81–7 |
| Butyl benzyl phthalate ....................... | 34292 | 85–68–7 |
| Di-n-butyl phthalate ........................... | 39110 | 84–74–2 |
| Diethyl phthalate ............................... | 34336 | 84–66–2 |
| Dimethyl phthalate ............................ | 34341 | 131–11–3 |
| Di-n-octyl phthalate ........................... | 34596 | 117–84–0 |

  - This is a gas chromatographic (GC) method  applicable  to  the  determination  of the compounds listed above in municipal and industrial discharges as  provided  under  40 CFR 136.1. When this method is used to  ana- lyze unfamiliar samples for any or all of the compounds above, compound identifications should be supported by  at  least  one  addi- tional qualitative technique. This method describes  analytical  conditions  for  a  second gas  chromatographic  column  that   can   be used  to  confirm  measurements  made  with the primary column. Method 625 provides gas chromatograph/mass spectrometer (GC/MS) conditions  appropriate  for   the   qualitative and  quantitative  confirmation  of  results   for all of the parameters listed above, using the extract  produced  by  this  method.

  - The method detection limit (MDL, de- fined in Section 14.1) 1 for each parameter is listed in Table 1. The MDL for a specific wastewater may differ from those listed, de- pending upon the nature of interferences  in the sample matrix.

  - The sample extraction and concentra- tion steps in this method are essentially the same as in Methods 608, 609, 611, and 612. Thus, a single sample may be extracted to measure the parameters included in the scope of each of these methods. When clean- up is required, the concentration levels must be high enough to permit selecting aliquots, as necessary, to apply appropriate cleanup procedures. The analyst is allowed the lati- tude, under Section 12, to select chromatographic conditions appropriate for the simultaneous measurement of combina- tions of these parameters.

  - Any modification of this method,  be- yond those expressly permitted, shall be con- sidered as a major modification subject to application and approval of alternate test procedures under 40 CFR 136.4 and 136.5.

  - This method is restricted to use by or under the supervision of analysts experi- enced in the use of a gas chromatograph and in the interpretation of gas chromatograms. Each analyst must demonstrate  the  ability to generate acceptable results with this method using the procedure described in Sec- tion 8.2.

#### 40 CFR Ch. I (7–1–17 Edition)

- Summary of Method

  - A measured volume of sample, ap- proximately 1–L, is extracted with  meth- ylene chloride using a separatory funnel. The methylene chloride extract is dried and ex- changed to hexane during concentration to a volume of 10 mL or less. The extract is sepa- rated by gas chromatography and the phthalate esters are then measured with an electron capture detector. 2

  - Analysis for phthalates is especially complicated by their ubiquitous occurrence in the environment. The method provides Florisil and alumina column cleanup proce- dures to aid in the elimination of inter- ferences that may be encountered.

- Interferences

  - Method interferences may be caused by contaminants in solvents, reagents, glass- ware, and other sample processing hardware that lead to discrete artifacts and/or ele- vated baselines in gas chromatograms. All of these materials must be routinely dem- onstrated to be free from interferences under the conditions of the analysis by running laboratory reagent blanks as described in Section 8.1.3.

    - Glassware must be scrupulously cleaned. 3 Clean all glassware as soon as pos- sible after use by rinsing with the last sol- vent used in it. Solvent rinsing should be fol- lowed by detergent washing with hot water, and rinses with tap water and distilled water. The glassware should then be drained dry, and heated in a muffle furnace at 400 C for 15 to 30 min. Some thermally stable ma- terials, such as PCBs, may not be eliminated by this treatment. Solvent rinses with ace- tone and pesticide quality hexane may be substituted for the muffle furnace heating. Thorough rinsing with such solvents usually eliminates PCB interference. Volumetric ware should not be heated in a muffle fur- nace. After drying and cooling, glassware should be sealed and stored in a clean envi- ronment to prevent any accumulation of dust or other contaminants. Store inverted or capped with aluminum foil.

    - The use of high purity reagents and solvents helps to minimize interference prob- lems. Purification of solvents  by  distillation in all-glass systems may be required.

  - Phthalate esters are contaminants in many products commonly found in the lab- oratory. It is particularly important to avoid the use of plastics because phthalates are commonly used as plasticizers and are easily extracted from plastic materials. Serious phthalate contamination can result at any time, if consistent quality control is not practiced. Great care must be experienced to prevent such contamination. Exhaustive cleanup of reagents and glassware may be re- quired to eliminate background phthalate contamination. 4 5

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 606

  - Matrix interferences may be caused by contaminants that are co-extracted from the sample. The extent of matrix interferences will vary considerably from source to source, depending upon the nature and diversity  of the industrial complex or municipality being sampled.  The  cleanup  procedures  in  Section

11 can be used to overcome many of these interferences, but unique samples may re- quire additional cleanup approaches to achieve the MDL listed in Table 1.

- Safety

4.1 The toxicity or  carcinogenicity  of each reagent used in this method has not been precisely defined; however, each chem- ical compound should be treated as a poten- tial health hazard. From this viewpoint, ex- posure to these chemicals must be reduced to the lowest possible level by whatever means available. The laboratory is responsible for maintaining a current awareness file of OSHA regulations regarding the safe han- dling of the chemicals specified in this meth- od. A reference file of material data handling sheets should also be made available to all personnel involved in the chemical analysis. Additional references to laboratory safety are available and have been identified 6 8 for the information of the analyst.

- Apparatus and Materials

  - Sampling equipment, for discrete or composite  sampling.

    - Grab sample bottle—1–L or 1–qt, amber glass, fitted with a screw cap lined with Teflon. Foil may be substituted for Tef- lon if the sample is not corrosive. If amber bottles are not available, protect samples from light. The bottle and cap liner must be washed, rinsed with acetone or methylene chloride, and dried before use to minimize contamination.

    - Automatic sampler (optional)—The sampler must incorporate glass sample con- tainers for the collection of a minimum of 250 mL of sample. Sample containers must be kept refrigerated at 4 C and protected from light during compositing. If the sampler uses a peristaltic pump, a minimum length of compressible silicone rubber tubing may be used. Before use, however, the compressible tubing should be thoroughly rinsed with methanol, followed by repeated rinsings with distilled water to minimize the potential for contamination of the sample. An integrating flow meter is required to collect flow propor- tional  composites.

  - Glassware (All specifications are sug- gested. Catalog numbers are included for il- lustration only).

    - Separatory funnel—2–L, with Teflon stopcock.

    - Drying column—Chromatographic column, approximately 400 mm long 19 mm ID,  with  coarse  frit  filter  disc.

    - Chromatographic column—300 mm long 10 mm ID, with Teflon stopcock and coarse frit filter disc at bottom (Kontes K– 420540–0213 or equivalent).

    - Concentrator tube, Kuderna-Dan- ish—10–mL, graduated (Kontes K–570050–1025 or equivalent). Calibration must  be  checked at the volumes employed in the test. Ground glass stopper is used to prevent evaporation of  extracts.

    - Evaporative flask, Kuderna-Danish— 500–mL (Kontes K–570001–0500 or equivalent). Attach  to  concentrator  tube  with  springs.

    - Snyder column, Kuderna-Danish— Three-ball macro (Kontes K–503000–0121 or equivalent).

    - Snyder column, Kuderna-Danish— Two-ball micro (Kontes K–569001–0219 or equivalent).

    - Vials—10 to 15–mL, amber glass, with Teflon-lined screw cap.

  - Boiling chips—Approximately 10/40 mesh. Heat to 400 C for 30 min or Soxhlet ex- tract  with  methylene  chloride.

  - Water bath—Heated, with concentric ring cover, capable of temperature control (2 C). The bath should be used in a hood.

  - Balance—Analytical, capable of accu- rately weighing 0.0001 g.

  - Gas chromatograph—An analytical system complete with gas chromatograph suitable for on-column injection and all re- quired accessories including syringes, ana- lytical columns, gases, detector, and strip- chart recorder. A data system is rec- ommended for measuring peak areas.

    - Column  1—1.8  m  long  4  mm  ID

glass, packed with 1.5% SP–2250/1.95% SP– 2401 Supelcoport (100/120 mesh) or equivalent. This column  was used  to  develop the  method performance statemelts in Section 14. Guide- lines  for  the  use  of   alternate   column packings are provided in Section 12.1.

    - Column  2—1.8  m  long  4  mm  ID

glass, packed with 3% OV–1 on Supelcoport (100/120 mesh) or equivalent.

    - Detector—Electron capture detector. This detector has proven effective in the analysis of wastewaters for the parameters listed in the scope (Section 1.1), and was used to develop the method performance state- ments in Section 14. Guidelines for the use of alternate detectors are provided in Section 12.1.

- Reagents

  - Reagent water—Reagent water is de- fined as a water in which  an  interferent  is not observed at the  MDL  of  the  parameters of  interest.

  - Acetone, hexane, isooctane, methylene chloride, methanol—Pesticide quality or equivalent.

  - Ethyl ether—nanograde, redistilled in glass if necessary.

    - Ethyl ether must be shown to be free of peroxides before it is used as indicated by

#### Pt. 136, App. A, Meth. 606

EM Laboratories Quant  test  strips.  (Avail- able from Scientific Products Co., Cat. No. P1126–8, and other suppliers.)

    - Procedures recommended for re- moval of peroxides are provided with the test strips. After cleanup, 20 mL of ethyl alcohol preservative must be added to each liter of ether.

  - Sodium sulfate—(ACS) Granular, an- hydrous. Several levels of purification  may be required in order to reduce background phthalate levels to an acceptable level: 1) Heat 4 h at 400 C in a shallow tray, 2) Heat

16 h at 450 to 500 C in a shallow tray, 3) Soxhlet  extract  with  methylene  chloride   for 48 h.

  - Florisil—PR grade (60/100 mesh). Pur- chase activated at 1250 F and store in the dark in glass containers with ground glass stoppers or foil-lined screw caps. To prepare for use, place 100 g of Florisil into a 500-mL beaker and heat for approximately 16 h at 40

C. After heating transfer to a 500-mL rea- gent bottle. Tightly seal and cool to room temperature. When cool add 3 mL of reagent water. Mix thoroughly by shaking or rolling for 10 min and let it stand for at least 2 h. Keep the bottle sealed tightly.

  - Alumina—Neutral activity Super  I, W200 series (ICN Life Sciences Group, No. 404583). To prepare for use, place 100 g of alu- mina into a 500-mL beaker and heat for ap- proximately 16 h at 400 C. After heating transfer to a 500-mL reagent bottle. Tightly seal and  cool  to  room  temperature.  When cool add 3 mL of reagent water. Mix thor- oughly by shaking or rolling  for  10  min  and let it stand for at least 2 h. Keep the bottle sealed    tightly.

  - Stock standard solutions (1.00 g/L)—

Stock standard solutions can be prepared from pure standard materials or purchased as certified solutions.

    - Prepare stock standard solutions by accurately weighing about 0.0100 g of pure material. Dissolve  the  material  in  isooctane and dilute to volume in a 10-mL volumetric flask. Larger volumes can be used at the con- venience of the analyst. When compound pu- rity is assayed to be  96%  or  greater,  the weight can be used without correction to cal- culate the concentration of the stock stand- ard. Commercially  prepared  stock  standards can be used at any concentration if they are certified by the manufacturer or by an inde- pendent  source.

    - Transfer the stock standard solu- tions into Teflon-sealed screw-cap bottles. Store at 4 C and protect from light. Stock standard solutions should be checked fre- quently for signs of degradation or evapo- ration, especially just prior to preparing calibration standards from them.

    - Stock standard solutions must be re- placed after six months, or sooner if com- parison with check standards indicates a problem.

#### 40 CFR Ch. I (7–1–17 Edition)

  - Quality control check sample con- centrate—See Section 8.2.1.

- Calibration

  - Establish gas chromatograph oper- ating conditions equivalent to those given in Table 1. The gas chromatographic system can be calibrated using the external standard technique (Section 7.2) or the internal stand- ard technique (Section 7.3).

  - External standard calibration proce- dure:

    - Prepared calibration standards at a minimum of three concentration levels  for each parameter of interest by adding vol- umes of one or more stock standards to a volumetric flask and diluting to volume with isooctane. One of the external standards should be at a concentration near, but above, the MDL (Table 1) and the other concentra- tions should correspond to the expected range of concentrations found in real sam- ples or should define the working range of the detector.

    - Using injections of 2 to 5 L, analyze each calibration standard according to Sec- tion 12 and tabulate peak height or area re- sponses against the mass injected. The re- sults can be used to prepare a calibration curve for each compound. Alternatively, if the ratio of response to amount injected (calibration factor) is a constant over the working range (<10% relative standard devi- ation, RSD), linearity through the origin can be assumed and the average ratio or calibra- tion factor can be used in place of a calibra- tion  curve.

  - Internal standard calibration proce- dure—To use this approach, the analyst must select one or more internal standards that are similar in analytical behavior to the compounds of interest. The analyst must fur- ther demonstrate that the measurement of the internal standard is not affected by method or matrix interferences. Because of these limitations, no internal standard  can be suggested that is applicable to all sam- ples.

    - Prepare calibration standards at a minimum of three concentration levels  for each parameter of interest by adding vol- umes of one or more stock standards to a volumetric flash. To each calibration stand- ard, add a known constant amount of one or more internal standards, and dilute to vol- ume with isooctane. One of the standards should be at a concentration near, but above, the MDL and the other concentrations should correspond to the expected range of concentrations found in real samples or should define the working range of the detec- tor.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 606

    - Using injections of 2 to 5 L, analyze each calibration standard according to Sec- tion 12 and tabulate peak height or area re- sponses against concentration for each com- pound and internal standard. Calculate re- sponse factors (RF) for each compound using Equation 1.

RF = (As)(Cis (Ais)(Cs)

Equation   1

where:

As  = Response for the parameter to be meas- ured.

Ais = Response for the internal standard.

Cis  = Concentration of the internal standard (g/L).

Cs   =  Concentration  of  the  parameter  to  be measured (g/L).

If the RF value over the working range is a constant (<10% RSD), the RF can be as- sumed to be invariant and the average RF can be used for calculations. Alternatively, the results can be used to plot a calibration curve of response ratios, As/Ais, vs. RF.

  - The working calibration curve, cali- bration factor, or RF must be verified on each working day by the measurement of one or more calibration standards. If the re- sponse for any parameter varies from the predicted response by more than 15%, a new calibration curve must be prepared for that compound.

  - Before using any cleanup procedure, the analyst must process a series of calibra- tion standards through the procedure to vali- date elution patterns and the absence of interferences from the reagents.

- Quality Control

  - Each laboratory that uses this method is required to operate a formal quality  con- trol program. The minimum requirements of this program consist of an initial demonstra- tion of laboratory capability and an ongoing analysis of spiked samples to evaluate and document data quality. The laboratory must maintain records to document the quality of data that is generated. Ongoing data quality checks are compared with established per- formance criteria to determine if the results of analyses meet the performance character- istics of the method. When results of sample spikes indicate atypical method perform- ance, a quality control check  standard  must be analyzed to confirm that the measure- ments were performed in an in-control mode of operation.

    - The analyst must make an initial, one-time, demonstration of the ability to generate acceptable accuracy and precision with this method. This  ability  is  established as described in Section 8.2.

    - In recognition of advances that are occurring in chromatography, the analyst is permitted certain options (detailed in Sec- tions 10.4, 11.1, and 12.1) to improve the sepa-

rations or lower the cost of measurements. Each time such a modification is  made  to the method, the analyst is required to repeat the procedure in Section 8.2.

    - Before processing any samples, the analyst must analyze a  reagent  water  blank to demonstrate that interferences from the analytical system and glassware are under control. Each time a set of samples is ex- tracted or reagents are changed, a reagent water blank must be processed as a safe- guard  against  laboratory  contamination.

    - The laboratory must, on an ongoing basis, spike and analyze a minimum of 10% of all samples to monitor and evaluate lab- oratory data quality. This procedure is de- scribed in Section 8.3.

    - The laboratory must, on an ongoing basis, demonstrate through the analyses of quality control  check standards  that  the op- eration of the measurement system is in con- trol.  This  procedure  is  described  in  Section

8.4. The frequency of the check standard analyses is equivalent to 10% of all samples analyzed but may be reduced if spike recov- eries from samples (Section 8.3) meet all specified quality control criteria.

    - The laboratory must maintain per- formance records to document the quality of data that is generated. This procedure is de- scribed in Section 8.5.

  - To establish the ability to generate acceptable accuracy and precision, the ana- lyst must perform the following operations.

    - A quality contrml (QC) check sample concentrate is required containing each pa- rameter of interest at the following con- centrations in acetone: butyl benzyl phthal- ate, 10 g/mL; bis(2-ethylhexyl) phthalate, 50

g/mL; di-n-octyl phthalate, 50 g/mL; any other phthlate, 25 g/mL. The QC check sam- ple  concentrate  must  be  obtained  from  the

U.S. Environmental Protection Agancy, En- vironmental Monitoring and Support Lab- oratory in Cincinnati, Ohio, if available. If not available from that source, the QC check sample concentrate must be obtained from another external source. If not  available from either source above, the QC check sam- ple concentrate must be prepared by the lab- oratory using stock standards prepared inde- pendently from those used for calibration.

    - Using a pipet, prepare QC check sam- ples at the test concentrations  shown  in Table 2 by adding 1.00 mL  of  QC  check  sam- ple concentrate to each  of  four  1–L  aliquots of  reagent  water.

    - Analyze the well-mixed QC check samples according to the  method  beginning in Section 10.

    - Calculate the average recovery (X¯ ) in

g/L, and the standard deviation of the re- covery (s) in g/L, for each parameter using the four results.

    - For each parameter compare s and X¯

with the corresponding acceptance criteria for   precision   and   accuracy,   respectively,

#### Pt. 136, App. A, Meth. 606

found in Table 2. If s and X¯ for all param- eters of interest meet the acceptance cri- teria, the system performance is acceptable and analysis of actual samples can begin. If

any individual s exceeds the precision limit or any individual X¯  falls outside the range

for accuracy, the system performance is un- acceptable for that parameter. Locate and correct the source of the problem and repeat the test for all parameters of interest begin- ning with Section 8.2.2.

  - The laboratory must, on an ongoing basis, spike at least 10% of the samples from each sample site being monitored to assess accuracy. For laboratories analyzing one to ten samples per month, at least one spiked sample per month is required.

    - The concentration of the spike in the sample should be determined as follows:

      - If, as in compliance monitoring, the concentration of a specific parameter in the sample is being checked against a regu- latory concentration limit, the spike should be at that limit or 1 to 5 times higher than the background concentration determined in Section 8.3.2, whichever concentration would be larger.

      - If the concentration of a specific parameter in the sample  is  not  being checked against a limit specific to that pa- rameter, the spike should be at the test con- centration in Section 8.2.2 or 1 to 5 times higher than the background concentration determined in Section 8.3.2, whichever con- centration would be larger.

      - If it is impractical to determine background levels before spiking (e.g., max- imum holding times will be exceeded), the spike concentration should be (1) the regu- latory concentration limit, if any; or, if none

(2) the larger of either 5  times  higher  than the expected  background  concentration  or the test concentration in Section 8.2.2.

    - Analyze one sample aliquot to deter- mine the background concentration (B) of each parameter. If necessary, prepare a new QC check sample concentrate (Section 8.2.1) appropriate for the background concentra- tions in the sample. Spike a second sample aliquot with 1.0 mL of the QC check sample concentrate and analyze it to determine the concentration after spiking (A) of each pa- rameter. Calculate each percent recovery (P) as 100(A-B)%/T, where T is the known true value of the spike.

    - Compare the percent recovery (P) for each parameter with the corresponding QC acceptance criteria found in Table 2. These acceptance criteria were calculated to in- clude an allowance for error in measurement of both the background and spike concentra- tions, assuming a spike to background ratio of 5:1. This error will be accounted for to the extent that the analyst’s spike to back- ground ratio approaches 5:1. 9 If spiking was performed at a concentration lower than the test concentration in Section 8.2.2, the ana-

#### 40 CFR Ch. I (7–1–17 Edition)

lyst must use either the QC acceptance cri- teria in Table 2, or optional QC acceptance criteria calculated for the specific spike con- centration. To calculate optional acceptance criteria for the recovery of a parameter: (1) Calculate accuracy (X) using the equation in Table 3, substituting the spike concentration

(T) for C; (2) calculate overall precision (S) using the equation in Table 3, substituting X for X¯ ; (3) calculate the range for recovery at

the spike concentration as (100 X/T)2.44(100 S/T)%. 9

    - If any individual P falls outside the designated range for recovery, that param- eter has failed the acceptance criteria. A check standard containing each parameter that failed the criteria must be analyzed as described in Section 8.4.

  - If any parameter fails the acceptance criteria for recovery in Section 8.3, a QC check standard containing each parameter that failed must be prepared and analyzed.

NOTE: The frequency for the required anal- ysis of a QC check standard will depend upon the number of parameters being simulta- neously tested, the complexity of the sample matrix, and the performance of the labora- tory.

    - Prepare the QC check standard by adding 1.0 mL of QC check sample con- centrate (Section 8.2.1 or 8.3.2) to 1 L of rea- gent water. The QC check standard needs only to contain the parameters that failed criteria in the test in Section 8.3.

    - Analyze the QC check standard to determine the concentration measured (A) of each parameter. Calculate each percent re- covery (Ps) as 100 (A/T)%, where T is the true value of the standard concentration.

    - Compare the percent recovery (Ps) for each parameter with the corresponding QC acceptance criteria found in Table 2. Only parameters that failed the test in Section 8.3 need to be compared with these  criteria.  If the recovery of any such parameter falls out- side the designated range, the laboratory performance for that parameter is judged to be out of control, and the problem must be immediately identified and corrected. The analytical result for that parameter in the unspiked sample is suspect  and may not  be reported for regulatory compliance purposes.

  - As part of the QC program for the lab- oratory, method accuracy for wastewater samples must be assessed and records must be maintained. After the analysis of five spiked wastewater samples as in Section 8.3,

calculate  the  average  percent  recovery  (P¯ )

and the standard deviation of the percent re- covery (sp). Express the accuracy assessment

as a percent recovery interval from P¯ ¥2sp to P¯ + 2sp. If P¯ = 90% and sp = 10%, for example,

the accuracy interval is expressed as 70– 110%. Update the accuracy  assessment  for each parameter on a regular basis (e.g. after each five to  ten  new  accuracy  measure- ments).

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 606

  - It is recommended that the laboratory adopt additional quality assurance practices for use  with  this method.  The  specific  prac- tices that  are  most  productive  depend  upon the needs of the laboratory and the nature of the samples. Field duplicates may be ana- lyzed to assess the precision of the environ- mental measurements. When doubt exists over the identification of a peak on the chro- matogram, confirmatory techniques such as gas chromatography with a dissimilar col- umn, specific element detector, or mass spectrometer must be used. Whenever pos- sible, the laboratory should analyze standard reference materials and participate in rel- evant performance evaluation studies.

- Sample Collection, Preservation, and Handling

  - Grab samples must be collected  in glass containers. Conventional sampling practices 10 should be followed, except that the bottle must not be prerinsed with sample before collection. Composite samples should be collected in refrigerated  glass  containers in accordance with the requirements of the program. Automatic sampling equipment must be as free as possible of Tygon tubing and other potential sources of contamina- tion.

  - All samples must be iced or refrig- erated at 4 C from the time of collection until   extraction.

  - All samples must be extracted within 7 days of collection and completely analyzed within 40 days of extraction. 2

- Sample Extraction

  - Mark the water meniscus on the side of the sample bottle for later determination of sample volume. Pour the entire sample into a 2–L separatory funnel.

  - Add 60 mL of methylene chloride  to the sample bottle, seal, and shake 30 s to rinse the inner surface. Transfer the solvent to the separatory funnel and extract the sample by shaking the funnel for 2 min. with periodic venting to release excess pressure. Allow the organic layer to separate from the water phase for a minimum of 10 min. If the emulsion interface between layers is more than one-third the volume of  the  solvent layer, the analyst must employ mechanical techniques to complete the phrase separa- tion. The optimum technique depends upon the sample, but may include stirring, filtra- tion of the emulsion through glass wool, cen- trifugation, or other physical methods. Col- lect the methylene chloride extract in a 250- mL  Erlenmeyer  flask.

  - Add a second 60-mL volume of meth- ylene chloride to the sample bottle and re- peat the extraction procedure a second time, combining the extracts in the Erlenmeyer flask. Perform a third extraction in the same manner.

  - Assemble a Kuderna-Danish (K-D) concentrator by attaching a 10-mL concen- trator tube to a 500-mL evaporative flask. Other concentrator devices or  techniques may be used in place of the K-D concentrator if the requirements of Section 8.2 are met.

  - Pour the combined extract through a solvent-rinsed drying column containing about 10 cm of anhydrous sodium sulfate, and collect the extract in the K-D concen- trator. Rinse the Erlenmeyer flask and col- umn with 20 to 30 mL of methylene chloride to complete the quantitative transfer.

  - Add one or two clean boiling chips to the evaporative flask and attach a three-ball Snyder column. Prewet the Snyder  column by adding about 1 mL of methylene chloride to the top. Place the K-D apparatus on a hot water bath (60 to 65 C) so that the concen- trator tube is partially immersed in the hot water, and the entire lower rounded surface of the flask is bathed with hot vapor. Adjust the vertical position of the apparatus  and the water temperature as required to com- plete the concentration in 15 to  20  min.  At the proper rate of distillation the balls of the column will actively chatter but the cham- bers will not flood with condensed solvent. When the apparent volume of liquid reaches 1 mL, remove the K-D apparatus and allow it to drain and cool for at least 10 min.

  - Increase the temperature of the hot water bath to about 80 C. Momentarily re- move the Snyder column, add 50 mL  of hexane and a new boiling chip,  and  reattach the  Snyder  column.  Concentrate   the   extract as in Section 10.6, except use hexane  to prewet the column. The elapsed time of con- centration should be 5 to 10 min.

  - Remove the Snyder column and rinse the flask and its lower joint into the concen- trator tube with 1 to 2 mL of hexane. A 5-mL syringe is recommended for this operation. Adjust the extract volume to 10 mL. Stopper the concentrator tube and store refrigerated if further processing will not be performed immediately. If the extract will be stored longer than two days, it should be trans- ferred to a Teflon-sealed screw-cap vial.  If the sample extract requires no further clean- up, proceed with gas chromatographic anal- ysis (Section 12). If the sample requires fur- ther cleanup, proceed to Section 11.

  - Determine the original sample vol- ume by refilling the sample bottle to the mark and transferring the liquid to  a  1000- mL graduated cylinder. Record the sample volume to the nearest 5 mL.

- Cleanup and Separation

11. Cleanup procedures may not be nec- essary for a relatively clean sample matrix. If particular circumstances demand the use of a cleanup procedure, the analyst may use either procedure below or any other appro- priate procedure. However, the analyst first must demonstrate that the requirements of

#### Pt. 136, App. A, Meth. 606

Section 8.2 can be met using the method as revised to incorporate the cleanup  proce- dure.

  - If the entire extract is to be cleaned up by one of the following procedures, it must be concentrated to 2.0 mL. To the con- centrator tube in Section 10.8, add a clean boiling chip and attach a two-ball micro- Snyder column. Prewet the column by add- ing about 0.5 mL of hexane to the top. Place the micro-K-D apparatus on a hot water bath (80 C) so that the concentrator tube is par- tially immersed in the hot water. Adjust the vertical position of the apparatus and the water temperature as required to complete the concentration in 5 to 10 min. At the prop- er rate of distillation the balls of the column will actively chatter but the chambers will not flood. When the apparent volume of liq- uid reaches about 0.5 mL, remove the K-D apparatus and allow it to drain and cool for at least 10 min. Remove the micro-Snyder column and rinse its lower joint into the concentrator tube with 0.2 mL of hexane. Ad- just the final volume to 2.0 mL and proceed with one of the following cleanup procedures.

  - Florisil column cleanup for phthalate esters:

    - Place 10 g of Florisil into a chromatographic column. Tap the column to settle the Florisil and add 1 cm of anhydrous sodium sulfate to the top.

    - Preelute the  column with  40 mL  of hexane. The rate for all elutions should be about 2 mL/min. Discard the eluate and just prior to exposure of the sodium sulfate layer to the air, quantitatively transfer the 2-mL sample extract onto the column using an ad- ditional 2  mL  of  hexane  to  complete  the transfer. Just prior to exposure of the so- dium sulfate layer to the air, add 40 mL of hexane and continue the elution of the col- umn. Discard this hexane eluate.

    - Next, elute the column  with  100  mL of 20% ethyl ether in hexane (V/V) into a 500- mL K-D flask equipped with a 10-mL concen- trator tube.  Concentrate  the  collected  frac- tion as in  Section  10.6.  No  solvent  exchange is necessary. Adjust  the  volume  of  the cleaned up extract to 10 mL in the concen- trator tube and analyze by  gas  chroma- tography  (Section  12).

  - Alumina column cleanup for phthal- ate esters:

    - Place 10 g of alumina into a chromatographic column. Tap the column to settle the alumina and add 1 cm of anhy- drous sodium sulfate to the top.

    - Preelute the  column with  40 mL  of hexane. The rate for all elutions should be about 2 mL/min. Discard the eluate and just prior to exposure of the sodium sulfate layer to the air, quantitatively transfer the 2-mL sample extract onto the column using an ad- ditional 2  mL  of  hexane  to  complete  the transfer. Just prior to exposure of the so- dium  sulfate  layer  to  the  air,  add  35  mL  of

#### 40 CFR Ch. I (7–1–17 Edition)

hexane and continue the elution of the col- umn. Discard this hexane eluate.

    - Next, elute the column  with  140  mL of 20% ethyl ether in hexane (V/V) into a 500- mL K-D flask equipped with a 10–mL concen- trator type.  Concentrate  the  collected  frac- tion as in  Section  10.6.  No  solvent  exchange is necessary. Adjust  the  volume  of  the cleaned up extract to 10 mL in the concen- trator tube and analyze by  gas  chroma- tography  (Section  12).

- Gas Chromatography

  - Table 1 summarizes the recommended operating conditions for the gas chro- matograph. Included in this table are reten- tion times and MDL that can be achieved under these conditions. Examples of the sep- arations achieved by Column 1 are shown in Figures 1 and 2. Other packed or capillary (open-tubular) columns, chromatographic conditions, or detectors may be used if the requirements of Section 8.2 are met.

  - Calibrate the system daily as de- scribed in Section 7.

  - If the internal standard calibration procedure is being used, the internal staldard must be added to the sample extract and mixed thoroughly immediately before injec- tion into the gas chromatograph.

  - Inject  2  to  5  L  of  the  sample  extract

or standard into  the  gas-chromatograph using the solvent-flush technique. 11 Smaller (1.0 L) volumes may be injected if auto- matic devices are employed. Record the vol- ume injected to the nearest 0.05 L, and the resulting peak size in area or peak height units.

  - Identify the parameters in the sample by comparing the retention times of the peaks in the sample chromatogram with those of the peaks in standard chromatograms. The width of the retention time window used to make identifications should be based upon measurements of ac- tual retention time variations of standards over the course of a day. Three times the standard deviation of a retention time for a compound can be used to calculate a sug- gested window size; however, the experience of the analyst should weigh heavily in the interpretation of chromatograms.

  - If the response for a peak exceeds the working range of the system, dilute the ex- tract and reanalyze.

  - If the measurement of the peak re- sponse is prevented by the presence of inter- ferences, further cleanup is required.

- Calculations

  - Determine the concentration of indi- vidual compounds in the sample.

    - If the external standard calibration procedure is used, calculate the amount of material injected from the peak response using  the  calibration  curve  or  calibration

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 606

factor determined in Section 7.2.2. The con- centration in the sample can be calculated from Equation 2.

AVt 

## Concentration (g/L) 

Vi Vs

Equation   2

where:

A = Amount of material injected (ng). Vi = Volume of extract injected (L). Vt = Volume of total extract (L).

Vs = Volume of water extracted (mL).

    - If the internal standard calibration procedure is used, calculate the concentra- tion in the sample using the response factor (RF) determined in Section 7.3.2 and Equa- tion 3.

As Is 

## Concentration (g/L) 

Ais RFVo 

Equation   3

where:

As  = Response for the parameter to be meas- ured.

Ais = Response for the internal standard.

Is   =  Amount  of  internal  standard  added  to each extract (g).

Vo = Volume of water extracted (L).

13.2 Report results in g/L without correc- tion for recovery data. All QC data obtained should be reported with the sample results.

- Method Performance

  - The method detection limit (MDL) is defined as the minimum concentration of a substance that can be measured and reported with 99% confidence that the value is above zero. 1 The MDL concentrations listed  in Table 1 were obtained using reagent water. 12 Similar results were achieved using rep- resentative wastewaters. The MDL actually achieved in a given analysis will vary de- pending on instrument sensitivity and ma- trix  effects.

  - This method has been tested for lin- earity of spike recovery from reagent water and has been demonstrated to be applicable over the concentration range from 5 MDL to 1000 MDL with the following exceptions: dimethyl and diethyl phthalate recoveries at 1000 MDL were low (70%); bis-2-ethylhexyl and di-n-octyl phthalate recoveries at 5  MDL were low (60%). 12

  - This method was tested by 16 labora- tories using reagent water, drinking water, surface water, and three industrial wastewaters spiked at six concentrations over the range 0.7 to 106 g/L. 13 Single oper- ator precision, overall precision, and method accuracy were found to be directly related to the  concentration  of  the  parameter  and  es-

sentially independent of the sample matrix. Linear equations to describe these relation- ships are presented in Table 3.

References

- 40 CFR part 136, appendix B.

- ‘‘Determination of Phthalates in Indus- trial and Muncipal Wastewaters,’’ EPA 600/4– 81–063, National Technical Information Serv- ice, PB81–232167, Springfield, Virginia 22161, July 1981.

- ASTM Annual Book of Standards, Part 31, D3694–78. ‘‘Standard Practices for Prepa- ration of Sample Containers and for Preser- vation of Organic Constituents,’’ American Society for Testing and Materials, Philadel- phia.

- Giam, C.S., Chan, H.S., and Nef, G.S. ‘‘Sensitive Method for Determination of Phthalate Ester Plasticizers in Open-Ocean Biota Samples,’’ Analytical Chemistry, 47, 2225 (1975).

- Giam, C.S., and Chan, H.S. ‘‘Control of Blanks in the Analysis of Phthalates in Air and Ocean Biota Samples,’’ U.S. National Bureau of Standards,  Special  Publication 442, pp. 701–708, 1976.

- ‘‘Carcinogens—Working with Carcino- gens,’’ Department of Health, Education, and Welfare, Public Health Service, Center for Disease Control, National Institute for Occu- pational Safety and Health, Publication No. 77–206, August 1977.

- ‘‘OSHA Safety and Health Standards, General Industry,’’ (29 CFR part 1910), Occu- pational Safety and Health Administration, OSHA 2206 (Revised, January 1976).

- ‘‘Safety in Academic Chemistry Labora- tories,’’ American Chemical Society Publica- tion, Committee on Chemical Safety, 3rd Edition, 1979.

- Provost  L.P.,  and  Elder,  R.S.  ‘‘Interpre- tation   of   Percent   Recovery   Data,’’   American Laboratory, 15, 58–63  (1983).  (The  value  2.44 used  in  the  equation  in  Section  8.3.3  is  two times the value 1.22 derived in this report.)

- ASTM Annual Book of Standards, Part 31, D3370–76. ‘‘Standard Practices for Sam- pling Water,’’ American Society for Testing and  Materials,  Philadelphia.

- Burke, J.A. ‘‘Gas Chromatography for Pesticide Residue Analysis; Some Practical Aspects,’’ Journal of the Association of Official Analytical Chemists, 48, 1037 (1965).

- ‘‘Method Detection Limit  and  Analyt- ical Curve Studies, EPA Methods 606, 607, and 608,’’ Special letter report for EPA Con- tract 68–03–2606, U.S. Environmental Protec- tion Agency, Environmental Monitoring and Support Laboratory, Cincinnati, Ohio 45268, June 1980.

- ‘‘EPA Method Study 16 Method 606 (Phthalate Esters),’’ EPA 600/4–84–056, Na- tional Technical Information Service, PB84– 211275, Springfield, Virginia 22161, June 1984.

#### Pt. 136, App. A, Meth. 606

40 CFR Ch. I (7–1–17 Edition)

TABLE 1—CHROMATOGRAPHIC CONDITIONS AND METHOD DETECTION LIMITS

| Parameter | Retention time (min) | Method de- tection limit (g/L) |
| --- | --- | --- |
|  | Column 1 | Column 2 |  |
| Dimethyl phthalate ................................................................................................... | 2.03 | 0.95 | 0.29 |
| Diethyl phthalate ...................................................................................................... | 2.82 | 1.27 | 0.49 |
| Di-n-butyl phthalate ................................................................................................. | 8.65 | 3.50 | 0.36 |
| Butyl benzyl phthalate ............................................................................................. | a 6.94 | a 5.11 | 0.34 |
| Bis(2-ethylhexyl) phthalate ...................................................................................... | a 8.92 | a 10.5 | 2.0 |
| Di-n-octyl phthalate ................................................................................................. | a 16.2 | a 18.0 | 3.0 |

Column 1 conditions: Supelcoport (100/120 mesh) coated with 1.5% SP–2250/1.95% SP–2401 packed in a 1.8 m long 4 mm ID glass column with 5% methane/95% argon carrier gas at 60 mL/min flow rate. Column temperature held isothermal at 180 C, except where otherwise indicated.

Column 2 conditions: Supelcoport (100/120 mesh) coated with 3% OV–1 packed in a 1.8 m long 4 mm ID glass column with 5% methane/95% argon carrier gas at 60 mL/min flow rate. Column temperature held isothermal at 200 C, except where other- wise indicated.

a 220 C column temperature.

TABLE 2—QC ACCEPTANCE CRITERIA—METHOD 606

| Parameter | Test conc. (g/ L) | Limit for s (g/L) | Range for X¯ (g/L) | Range for P, Ps (percent) |
| --- | --- | --- | --- | --- |
| Bis(2-ethylhexyl) phthalate .................................................................................. | 50 | 38.4 | 1.2–55.9 | D–158 |
| Butyl benzyl phthalate ......................................................................................... | 10 | 4.2 | 5.7–11.0 | 30–136 |
| Di-n-butyl phthalate ............................................................................................. | 25 | 8.9 | 10.3–29.6 | 23–136 |
| Diethyl phthalate ................................................................................................. | 25 | 9.0 | 1.9–33.4 | D–149 |
| Dimethyl phathalate ............................................................................................ | 25 | 9.5 | 1.3–35.5 | D–156 |
| Di-n-octyl phthalate ............................................................................................. | 50 | 13.4 | D–50.0 | D–114 |

s = Standard deviation of four recovery measurements, in g/L (Section 8.2.4). X¯ = Average recovery for four recovery measurements, in g/L (Section 8.2.4).

P, Ps  = Percent recovery measured (Section 8.3.2, Section 8.4.2). D = Detected; result must be greater than zero.

Note: These criteria are based directly upon the method performance data in Table 3. Where necessary, the limits for recovery have been broadened to assure applicability of the limits to concentrations below those used to develop Table 3.

TABLE 3—METHOD ACCURACY AND PRECISION AS FUNCTIONS OF CONCENTRATION—METHOD 606

| Parameter | Accuracy, as recovery, X (g/L) | Single analyst precision, sr (g/L) | Overall preci- sion, S(g/L) |
| --- | --- | --- | --- |
| Bis(2-ethylhexyl) phthalate ................................................................................ | 0.53C + 2.02 | 0.80X¯ ¥2.54 | 0.73X¯ ¥0.17 |
| Butyl benzyl phthalate ....................................................................................... | 0.82C + 0.13 | 0.26X¯ + 0.04 | 0.25X¯ + 0.07 |
| Di-n-butyl phthalate ........................................................................................... | 0.79C + 0.17 | 0.23X¯ + 0.20 | 0.29X¯ + 0.06 |
| Diethyl phthalate ................................................................................................ | 0.70C + 0.13 | 0.27X¯ + 0.05 | 0.45X¯ + 0.11 |
| Dimethyl phthalate ............................................................................................. | 0.73C + 0.17 | 0.26X¯ + 0.14 | 0.44X¯ + 0.31 |
| Di-n-octyl phthalate ........................................................................................... | 0.35C¥0.71 | 0.38X¯ + 0.71 | 0.62X¯ + 0.34 |

X¯ = Expected recovery for one or more measurements of a sample containing a concentration of C, in g/L.

sr= Expected single analyst standard deviation of measurements at an average concentration found of X¯ , in g/L. S= Expected interlaboratory standard deviation of measurements at an average concentration found of X¯ , in g/L. C = True value for the concentration, in g/L.

X¯ = Average recovery found for measurements of samples containing a concentration of C, in g/L.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 606

Pt. 136, App. A, Meth. 606

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 607

METHOD  607—NITROSAMINES

- Scope and Application

  - This method covers the determination of certain nitrosamines. The following pa- rameters can be determined by this method:

| Parameter | Storet No. | CAS No. |
| --- | --- | --- |
| N-Nitrosodimethylamine ............ | 34438 | 62–75–9 |
| N-Nitrosodiphenylamine ............ | 34433 | 86–30–6 |
| N-Nitrosodi-n-propylamine ......... | 34428 | 621–64–7 |

  - This is a gas chromatographic (GC) method  applicable  to  the  determination  of the parameters listed above in municipal and industrial discharges as  provided  under  40 CFR 136.1. When this method is used to  ana- lyze unfamiliar samples for any or all of the compmunds above, compound identifications should be supported by  at  least  one  addi- tional qualitative technique. This method describes analytical conditimns for a second gas  chromatographic  column  that   can   be used  to  confirm  measurements  made  with the primary column. Method 625 provides gas chromatograph/mass spectrometer (GC/MS) conditions  appropriate  for   the   qualitative and quantitative confirmation of results for N-nitrosodi-n-propylamine. In order to  con- firm	the	presence	of	N- nitrosodiphenylamine, the cleanup procedure specified in Section 11.3 or 11.4 must be used. In order to confirm the presence of N- nitrosodimethylamine  by  GC/MS,  Column   1 of this method must be substituted for the column recommended in Method 625. Con- firmation of these parameters using GC-high resolution mass  spectrometry  or  a Thermal Energy  Analyzer  is  also  recommended. 1 2

  - The method detection limit (MDL, de- fined in Section 14.1) 3 for each parameter is listed in Table 1. The MDL for a specific wastewater may differ from those listed, de- pending upon the nature of interferences  in the sample matrix.

  - Any modification of this method,  be- yond those expressly permitted, shall be con- sidered as a major modification subject to application and approval of alternate test procedures under 40 CFR 136.4 and 136.5.

  - This method is restricted to use by or under the supervision of analysts experi- enced in the use of a gas chromatograph and in the interpretation of gas chromatograms. Each analyst must demonstrate  the  ability to generate acceptable results with this method using the procedure described in Sec- tion 8.2.

- Summary of Method

  - A measured volume of sample, ap- proximately 1–L, is extracted with meth- ylene chloride using a separatory funnel. The methylene chloride extract is washed with dilute hydrochloric acid to remove free amines, dried, and concentrated to a volume

of 10 mL or less. After the extract has been exchanged to methanol, it is separated  by gas chromatography and the parameters are then measured with a nitrogen-phosphorus detector. 4

  - The method provides Florisil and alu- mina column cleanup procedures to separate diphenylamine from the nitrosamines and to aid in the elimination of interferences that may be encountered.

- Interferences

  - Method interferences may be caused by contaminants in solvents, reagents, glass- ware, and other sample processing hardware that lead to discrete artifacts and/or ele- vated baselines in gas chromatograms. All of these materials must be routinely dem- onstrated to be free from interferences under the conditions of the analysis by running laboratory reagent blanks as described in Section 8.1.3.

    - Glassware must be scrupulously cleaned. 5 Clean all glassware as soon as pos- sible after use by rinsing with the last  sol- vent used in it. Solvent rinsing should be fol- lowed by detergent washing with hot water, and rinses with tap water and distilled water. The glassware should then be drained dry, and heated in a muffle furnace at 400 C for 15 to 30 min. Solvent rinses with acetone and pesticide quality hexane may be sub- stituted for the muffle furnace heating. Vol- umetric ware should not be heated in a muf- fle furnace. After drying and cooling, glass- ware should be sealed and stored in a clean environment to prevent any accumulation of dust or other contaminants.  Store  inverted or capped with aluminum foil.

    - The use of high purity reagents and solvents helps to minimize interference prob- lems. Purification of solvents  by  distillation in all-glass systems may be required.

  - Matrix interferences may be caused by contaminants that are co-extracted from the sample. The extent of matrix interferences will vary considerably from source to source, depending upon the nature and diversity  of the industrial complex or municipality being sampled.  The  cleanup  procedures  in  Section

11 can be used to overcome many of these interferences, but unique samples may re- quire additional cleanup approaches to achieve the MDL listed in Table 1.

  - N-Nitrosodiphenylamine	is	re- ported 6M9  to undergo transnitrosation reac- tions. Care must be exercised in the heating or concentrating of solutions  containing this compound    in    the    presence    of    reactive amines.

  - The sensitive and selective Thermal Energy Analyzer and the reductive Hall de- tector may be used in place of the nitrogen- phosphorus detector when interferences are encountered. The Thermal Energy Analyzer offers the highest selectivity of the non-MS detectors.

#### Pt. 136, App. A, Meth. 607

- Safety

  - The   toxicity   or   carcinogenicity   of each  reagent  used  in  this  method  has  not been precisely defined; however, each chem- ical compound should be treated as a poten- tial health hazard. From this viewpoint, ex- posure to these chemicals must be reduced to the lowest possible level by whatever means available. The laboratory is responsible for maintaining   a   current   awareness   file   of OSHA  regulations  regarding  the  safe  han- dling of the chemicals specified in this meth- od. A reference file of material data handling sheets should also be made available to all personnel involved in the chemical analysis. Additional  references  to  laboratory  safety are available and have been identified 10M12 for the information of the analyst.

  - These  nitrosamines  are  known  car- cinogens, 13M17  therefore, utmost care must be exercised in the handling of these mate- rials.  Nitrosamine  reference  standards  and standard  solutions  should  be  handled  and prepared in a ventilated glove box within a properly ventilated room.

- Apparatus and Materials

  - Sampling equipment, for discrete or composite  sampling.

    - Grab sample bottle—1–L or 1-qt, amber glass, fitted with a screw cap lined with Teflon. Foil may be substituted for Tef- lon if the sample is not corrosive. If amber bottles are not available, protect samples from light. The bottle and cap liner must be washed, rinsed with acetone or methylene chloride, and dried before use to minimize contamination.

    - Automatic sampler (optional)—The sampler must incorporate glass sample con- tainers for the collection of a minimum of 250 mL of sample. Sample containers must be kept refrigerated at 4 C and protected from light during compositing. If the sampler uses a peristaltic pump, a minimum length of compressible silicone rubber tubing may be used. Before use, however, the compressible tubing should be thoroughly rinsed with methanol, followed by repeated rinsings with distilled water to minimize the potential for contamination of the sample. An integrating flowmeter is required to collect flow propor- tional  composites.

  - Glassware (All specifications are sug- gested. Catalog numbers are included for il- lustration only.):

    - Separatory funnels—2–L and 250–mL, with Teflon stopcock.

    - Drying column—Chromatographic column, approximately 400 mm long 19 mm ID,  with  coarse  frit  filter  disc.

    - Concentrator tube, Kuderna-Dan- ish—10-mL, graduated (Kontes K–570050–1025 or equivalent). Calibration must  be  checked at the volumes employed in the test. Ground

#### 40 CFR Ch. I (7–1–17 Edition)

glass stopper is used to prevent evaporation of  extracts.

    - Evaporative flask, Kuderna-Danish— 500-mL (Kontes K–570001–0500 or equivalent). Attach  to  concentrator  tube  with  springs.

    - Snyder column, Kuderna-Danish— Three-ball macro (Kontes K–503000–0121 or equivalent).

    - Snyder column, Kuderna-Danish— Two-ball micro (Kontes K–569001–0219 or equivalent).

    - Vials—10 to 15-mL, amber glass, with Teflon-lined screw cap.

    - Chromatographic column—Approxi- mately 400 mm long 22 mm ID, with Teflon stopcock and coarse frit filter disc at bottom (Kontes K–420540–0234 or equivalent), for use in Florisil column cleanup procedure.

    - Chromatographic column—Approxi- mately 300 mm long 10 mm ID, with Teflon stopcock and coarse frit filter disc at bottom (Kontes K–420540–0213 or equivalent), for use in alumina column cleanup procedure.

  - Boiling chips—Approximately 10/40 mesh. Heat to 400 C for 30 min or Soxhlet ex- tract  with  methylene  chloride.

  - Water bath—Heated, with concentric ring cover, capable of temperature control (2 C). The bath should be used in a hood.

  - Balance—Analytical, capable of accu- rately weighing 0.0001 g.

  - Gas chromatograph—An analytical system complete with gas chromatograph suitable for on-column injection and all re- quired accessories including syringes, ana- lytical columns, gases, detector, and strip- chart recorder. A data system is rec- ommended for measuring peak areas.

    - Column  1—1.8  m  long  4  mm  ID

glass, packed with 10% Carbowax 20 M/2% KOH on Chromosorb W-AW (80/100 mesh) or equivalent. This column was used to  develop the method performance statements in Sec- tion 14. Guidelines for the use of alternate column  packings  are  provided   in   Section 12.2.

    - Column  2—1.8  m  long  4  mm  ID

glass, packed with 10% SP–2250 on Supel- coport (100/120 mesh) or equivalent.

    - Detector—Nitrogen-phosphorus, re- ductive Hall, or Thermal Energy Analyzer detector. 1 2 These detectors have proven ef- fective in the analysis of wastewaters for the parameters listed in the scope (Section 1.1). A nitrogen-phosphorus detector was used to develop the method performance statements in Section 14. Guidelines for the use of alter- nate detectors are provided in Section 12.2.

- Reagents

  - Reagent water—Reagent water is de- fined as a water in which an  interferent  is not observed at the  MDL  of  the  parameters of  interest.

  - Sodium hydroxide solution (10 N)— Dissolve 40 g of NaOH (ACS) in reagent water and dilute to 100 ml.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 607

  - Sodium thiosulfate—(ACS) Granular.

  - Sulfuric acid (1 + 1)—Slowly, add  50 mL of  H2SO4 (ACS, sp.  gr.  1.84) to  50  mL of reagent water.

  - Sodium sulfate—(ACS) Granular, an- hydrous. Purify by heating at 400 C for 4 h in a shallow tray.

  - Hydrochloric acid (1 + 9)—Add one vol- ume of concentrated HCl (ACS) to nine vol- umes of reagent water.

  - Acetone, methanol, methylene chlo- ride, pentane—Pesticide quality or equiva- lent.

  - Ethyl ether—Nanograde, redistilled in glass if necessary.

    - Ethyl ether must be shown to be free of peroxides before it is used as indicated by EM Laboratories Quant  test  strips.  (Avail- able from Scientific Products Co., Cat No. P1126–8, and other suppliers.)

    - Procedures recommended for re- moval of peroxides are provided with the test strips. After cleanup, 20 mL of ethyl alcohol preservative must be added to each liter of ether.

  - Florisil—PR grade (60/100 mesh). Pur- chase activated at 1250 F and store in the dark in glass containers with ground glass stoppers or foil-lined screw caps. Before use, activate each batch at least 16 h at 130 C in a foil-covered glass container and allow to cool.

  - Alumina—Basic  activity  Super   I, W200 series (ICN Life Sciences Group, No. 404571, or equivalent). To prepare for use, place 100 g of alumina into a 500-mL reagent bottle and add 2 mL of  reagent  water.  Mix the alumina preparation  thoroughly  by shaking or  rolling  for 10  min  and let  it stand for at least 2 h. The preparation should be homogeneous before use. Keep the bottle sealed  tightly  to  ensure  proper  activity.

  - Stock    standard    solutions    (1.00    g/

L)—Stock standard solutions can be pre- pared from pure standard materials or pur- chased as certified solutions.

    - Prepare stock standard solutions by accurately weighing about 0.0100 g of pure material. Dissolve  the  material  in  methanol and dilute to volume in a 10-mL volumetric flask. Larger volumes can be used at the con- venience of the analyst. When compound pu- rity is assayed to be  96%  or  greater,  the weight can be used without correction to cal- culate the concentration of the stock stand- ard. Commercially  prepared  stock  standards can be used at any concentration if they are certified by the manufacturer or by an inde- pendent  source.

    - Transfer the stock standard solu- tions into Teflon-sealed screw-cap bottles. Store at 4 C and protect from light. Stock standard solutions should be checked fre- quently for signs of degradation or evapo- ration, especially just prior to preparing calibration standards from them.

    - Stock standard solutions must be replaced after six months, or sooner if com- parison with check standards indicates a problem.

6.12 Quality control check sample con- centrate—See Section 8.2.1.

- Calibration

  - Establish gas chromatographic oper- ating conditions equivalent to those given in Table 1. The gas chromatographic system can be calibrated using the external standard technique (Section 7.2) or the internal stand- ard technique (Section 7.3).

  - External standard calibration proce- dure:

    - Prepare calibration standards at a minimum of three concentration levels  for each parameter of interest by adding vol- umes of one or more stock standards to a volumetric flask and diluting to volume with methanol. One of the external standards should be at a concentration near, but above, the MDL (Table 1) and the other concentra- tions should correspond to the expected range of concentrations found in real sam- ples or should define the working range of the detector.

    - Using injections of 2 to 5 L, analyze each calibration standard according to Sec- tion 12 and tabulate peak height or area re- sponses against the mass injected. The re- sults can be used to prepare a calibration curve for each compound. Alternatively, if the ratio of response to amount injected (calibration factor) is a constant over the working range (<10% relative standard devi- ation, RSD), linearity through the origin can be assumed and the average ratio or calibra- tion factor can be used in place of a calibra- tion  curve.

  - Internal standard calibration proce- dure—To use this approach, the analyst must select one or more internal standards that are similar in analytical behavior to the compounds of interest. The analyst must fur- ther demonstrate that the measurement of the internal standard is not affected by method or matrix interferences. Because of these limitations, no internal standard  can be suggested that is applicable to all sam- ples.

    - Prepare calibration standards at a minimum of three concentration levels  for each parameter of interest by adding vol- umes of one or more stock standards to a volumetric flask. To each calibration stand- ard, add a known constant amount of one or more internal standards, and dilute to vol- ume with methanol. One of the standards should be at a concentration near, but above, the MDL and the other concentrations should correspond to the expected range of concentrations found in real samples or should define the working range of the detec- tor.

#### Pt. 136, App. A, Meth. 607

    - Using injections of 2 to 5 L, analyze each calibration standard according to Sec- tion 12 and tabulate peak height or area re- sponses against concentration for each com- pound and internal standard. Calculate re- sponse factors (RF) for each compound using Equation 1.

RF = (As)(Cis (Ais)(Cs)

Equation   1

where:

As  = Response for the parameter to be meas- ured.

Ais = Response for the internal standard.

Cis  = Concentration of the internal standard (g/L).

Cs   =  Concentration  of  the  parameter  to  be measured (g/L).

If the RF value over the working range is a constant (<10% RSD), the RF can be as- sumed to be invariant and the average RF can be used for calculations. Alternatively, the results can be used to plot a calibration curve of response ratios, As/Ais, vs. RF.

  - The working calibration curve, cali- bration factor, or RF must be verified on each working day by the measurement of one or more calibration standards. If the re- sponse for any parameter varies from the predicted response by more than 15%, a new calibration curve must be prepared for that compound.

  - Before using any cleanup procedure, the analyst must process a series of calibra- tion standards through the procedure to vali- date elution patterns and the absence of interferences from the reagents.

- Quality Control

  - Each laboratory that uses this method is required to operate a formal quality  con- trol program. The minimum requirements of this program consist of an initial demonstra- tion of laboratory capability and an ongoing analysis of spiked samples to evaluate and document data quality. The laboratory must maintain records to document the quality of data that is generated. Ongoing data quality checks are compared with established per- formance criteria to determine if the results of analyses meet the performance character- istics of the method. When results of sample spikes indicate atypical method perform- ance, a quality control check  standard  must be analyzed to confirm that the measure- ments were performed in an in-control mode of operation.

    - The analyst must make an initial, one-time, demonstration of the ability to generate acceptable accuracy and precision with this method. This  ability  is  established as described in Section 8.2.

    - In recognition of advances that are occurring in chromatography, the analyst is permitted certain options (detailed in Sec- tions 10.4, 11.1, and 12.2) to improve the sepa-

#### 40 CFR Ch. I (7–1–17 Edition)

rations or lower the cost of measurements. Each time such a modification is  made  to the method, the analyst is required to repeat the procedure in Section 8.2.

    - Before processing any samples, the analyst must analyze a  reagent  water  blank to demonstrate that interferences from the analytical system and glassware are under control. Each time a set of samples is ex- tracted or reagents are changed, a reagent water blank must be processed as a safe- guard  against  laboratory  contamination.

    - The laboratory must, on an ongoing basis, spike and analyze a minimum of 10% of all samples to monitor and evaluate lab- oratory data quality. This procedure is de- scribed in Section 8.3.

    - The laboratory must, on an ongoing basis, demonstrate through the analyses of quality control  check standards  that  the op- eration of the measurement system is in con- trol.  This  procedure  is  described  in  Section

8.4. The frequency of the check standard analyses is equivalent to 10% of all samples analyzed but may be reduced if spike recov- eries from samples (Section 8.3) meet all specified quality control criteria.

    - The laboratory must maintain per- formance records to document the quality of data that is generated. This procedure is de- scribed in Section 8.5.

  - To establish the ability to generate acceptable accuracy and precision, the ana- lyst must perform the following operations.

    - A quality control (QC) check sample concentrate is required containing each pa- rameter of  interest  at a  concentration  of  20

g/mL in methanol. The QC check sample concentrate must be obtained from the U.S. Environmental Protection Agency, Environ- mental Monitoring and Support Laboratory in Cincinnati, Ohio, if available. If not avail- able from that source, the QC check sample concentrate must be obtained from another external source. If not available from either source above, the QC check sample con- centrate must be prepared by the laboratory using stock standards prepared independ- ently from those used for calibration.

    - Using a pipet, prepare QC check sam- ples at a concentration of 20 g/L by adding

1.00 mL of QC check sample concentrate to each of four 1–L aliquots of reagent water.

    - Analyze the well-mixed QC check samples according to the  method  beginning in Section 10.

    - Calculate the average recovery (X¯ ) in

g/L, and the standard deviation of the re- covery (s) in g/L, for each parameter using the four results.

    - For each parameter compare s and X¯

with the corresponding acceptance criteria for   precision   and   accuracy,   respectively,

found in Table 2. If s and X¯  for all param-

eters of interest meet the acceptance cri- teria, the system performance is acceptable and analysis of actual samples can begin. If

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 607

any individual s exceeds the precision limit or any individual X¯  falls outside the range

for accuracy, the system performance is un- acceptable for that parameter. Locate and correct the source of the problem and repeat the test for all parameters of interest begin- ning with Section 8.2.2.

  - The laboratory must, on an ongoing basis, spike at least 10% of the samples from each sample site being monitored to assess accuracy. For laboratories analyzing one to ten samples per month, at least one spiked sample per month is required.

    - The concentration of the spike in the sample should be determined as follows:

      - If, as in compliance monitoring, the concentration of a specific parameter in the sample is being checked against a regu- latory concentration limit, the spike should be at that limit or 1 to 5 times higher than the background concentration determined in Section 8.3.2, whichever concentration would be larger.

      - If the concentration of a specific parameter in the sample  is  not  being checked against a limit specific to that pa- rameter, the spike should be at 20 g/L or 1 to 5  times  higher than  the  background  con- centration determined in Section 8.3.2, whichever concentration would be larger.

      - If it is impractical to determine background levels before spiking (e.g., max- imum holding times will be exceeded), the spike concentration should be (1) the regu- latory concentration limit, if any; or, if none

(2) the larger of either 5  times  higher  than the expected background concentration or 20

g/L.

    - Analyze one sample aliquot to deter- mine the background concentration (B) of each parameter. If necessary, prepare a new QC check sample concentrate (Section 8.2.1) appropriate for the background concentra- tions in the sample. Spike a second sample aliquot with 1.0 mL of the QC check sample concentrate and analyze it to determine the concentration after spiking (A) of each pa- rameter. Calculate each percent recovery (P) as 100(A¥B)%/T, where T is the known true value of the spike.

    - Compare the percent recovery (P) for each parameter with the corresponding QC acceptance criteria found in Table 2. These acceptance criteria were caluclated to in- clude an allowance for error in measurement of both the background and spike concentra- tions, assuming a spike  to  background  ratio of 5:1. This error will be accounted for to the extent that the analyst’s spike to back- ground ratio approaches 5:1. 18 If spiking was performed at a concentration lower than 20

g/L, the analyst must use either the QC ac- ceptance criteria in Table 2, or optional QC acceptance criteria  caluclated for  the spe- cific spike concentration. To calculate op- tional acceptance criteria for the recovery of a   parameter:   (1)   Calculate   accuracy   (X)

using the equation in Table 3,  substituting the spike concentration (T) for C; (2) cal- culate  overall  precision  (S)  using  the  equa-

tion in Table 3, substituting Xfor X¯ ; (3) cal-

culate the range for recovery at the spike concentration as (100 X/T) 2.44(100 S/T)%. 18

    - If any individual P falls outside the designated range for recovery, that param- eter has failed the acceptance criteria. A check standard containing each parameter that failed the criteria must be analyzed as described in Section 8.4.

  - If any parameter fails the acceptance criteria for recovery in Section 8.3, a QC check standard containing each parameter that failed must be prepared and analyzed.

NOTE: The frequency for the required anal- ysis of a QC check standard will depend upon the number of parameters being simulta- neously tested, the complexity of the sample matrix, and the performance of the labora- tory.

    - Prepare the QC check standard by adding 1.0 mL of QC check sample con- centrate (Section 8.2.1 or 8.3.2) to 1 L of rea- gent water. The QC check standard needs only to contain the parameters that failed criteria in the test in Section 8.3.

    - Analyze the QC check standard to determine the concentration measured (A) of each parameter. Calculate each percent re- covery (Ps) as 100 (A/T)%, where T is the true value of the standard concentration.

    - Compare the percent recovery (Ps) for each parameter with the corresponding QC acceptance criteria found in Table 2. Only parameters that failed the test in Section 8.3 need to be compared with these  criteria.  If the recovery of any such parameter falls out- side the designated range, the laboratory performance for that parameter is judged to be out of control, and the problem must be immediately identified and corrected. The analytical result for that parameter in the unspiked sample is suspect  and may not  be reported for regulatory compliance purposes.

  - As part of the QC program for the lab- oratory, method accuracy for wastewater samples must be assessed and records must be maintained. After the analysis of five spiked wastewater samples as in Section 8.3,

calculate  the  average  percent  recovery  (P¯ )

and the standard deviation of the percent re- covery (sp). Express the accuracy assessment

as a percent recovery interval from P¯ ¥2sp to P¯ + 2sp. If P¯ = 90% and sp = 10%, for example,

the accuracy interval is expressed as 70– 110%. Update the accuracy  assessment  for each parameter on a regular basis (e.g. after each five to  ten  new  accuracy  measure- ments).

  - It is recommended that the laboratory adopt additional quality assurance practices for use with this method. The specific prac- tices that are most productive depend upon the needs of the laboratory and the nature of

#### Pt. 136, App. A, Meth. 607

the samples. Field duplicates may be ana- lyzed to assess the precision of the environ- mental measurements. When doubt exists over the identification of a peak on the chro- matogram, confirmatory techniques such as gas chromatography with a dissimilar col- umn, specific element detector, or mass spectrometer must be used. Whenever pos- sible, the laboratory should analyze standard reference materials and participate in rel- evant performance evaluation studies.

- Sample Collection, Preservation, and Handling

  - Grab samples must be collected  in glass containers. Conventional sampling practices 19 should be followed, except that the bottle must not be prerinsed with sample before collection. Composite samples should be collected in refrigerated  glass  containers in accordance with the requirements of the program. Automatic sampling equipment must be as free as possible of Tygon tubing and other potential sources of contamina- tion.

  - All samples must be iced or refrig- erated at 4 C from the time of collection until extraction.  Fill  the  sample  bottles  and, if residual chlorine is present, add 80 mg of sodium thiosulfate per liter of sample and mix well. EPA Methods 330.4 and 330.5 may be used for measurement of residual chlo- rine. 20 Field test kits are available for this purpose. If N-nitrosodiphenylamine is to be determined, adjust the sample pH to 7 to 10 with sodium hydroxide solution or sulfuric acid.

  - All samples must be extracted within 7 days of collection and completely analyzed within 40 days of extraction. 4

  - Nitrosamines are known to be light sensitive. 7 Samples should be stored in amber or foil-wrapped bottles in order to minimize  photolytic  decomposition.

- Sample Extraction

  - Mark the water meniscus on the side of the sample bottle  for  later  determination of sample volume. Pour the entire sample into a 2–L separatory  funnel.  Check  the  pH of the sample with wide-range pH paper and adjust to within the range of 5 to 9 with so- dium hydroxide solution or sulfuric acid.

  - Add 60 mL of methylene chloride  to the sample bottle, seal, and shake 30 s to rinse the inner surface. Transfer the solvent to the separatory funnel and extract the sample by shaking the funnel for 2 min with periodic venting to release excess pressure. Allow the organic layer to separate from the water phase for a minimum of 10 min. If the emulsion interface between layers is more than one-third the volume of  the  solvent layer, the analyst must employ mechanical techniques to complete the phase separation. The  optimum  technique  depends  upon  the

#### 40 CFR Ch. I (7–1–17 Edition)

sample, but may include  stirring,  filtration of the emulsion through glass wool, cen- trifugation, or other physical methods. Col- lect the methylene chloride extract in a 250- mL Erlenmeyer flask.

  - Add a second 60-mL volume of meth- ylene chloride to the sample bottle and re- peat the extraction procedure a second time, combining the extracts in the Erlenmeyer flask. Perform a third extraction in the same manner.

  - Assemble a Kuderna-Danish (K-D) concentrator by attaching a 10-mL concen- trator tube to a 500-mL evaporative flask. Other concentration devices or  techniques may be used in place of the K-D concentrator if the requirements of Section 8.2 are met.

  - Add 10 mL of hydrochloric acid to the combined extracts and shake for  2  min. Allow the layers to separate. Pour the com- bined extract through a solvent-rinsed dry- ing column containing about 10 cm of anhy- drous sodium sulfate, and collect the extract in the K-D concentrator. Rinse the Erlen- meyer flask and column with 20 to 30 mL of methylene chloride to complete the quan- titative   transfer.

  - Add one or two clean boiling chips to the evaporative flask and attach a three-ball Snyder column. Prewet the Snyder  column by adding about 1 mL of methylene chloride to the top. Place the K-D apparatus on a hot water bath (60 to 65 C) so that the concen- trator tube is partially immersed in the hot water, and the entire lower rounded surface of the flask is bathed with hot vapor. Adjust the vertical position of the apparatus  and the water temperature as required to com- plete the concentration in 15 to  20  min.  At the proper rate of distillation the balls of the column will actively chatter but the cham- bers will not flood with condensed solvent. When the apparent volume of liquid reaches 1 mL, remove the K-D apparatus and allow it to drain and cool for at least 10 min.

  - Remove the Snyder column and rinse the flask and its lower joint into the concen- trator tube with 1 to 2 mL of methylene chloride. A 5-mL syringe is recommended for this  operation.  Stopper  the  concentrator tube and store refrigerated if further proc- essing will not be performed immediately. If the extract will be stored longer than two days, it should be transferred to a Teflon- sealed	screw-cap	vial.	If	N- nitrosodiphenylamine is to be measured by gas chromatography, the analyst must first use a cleanup column to eliminate diphenylamine interference (Section 11). If N-nitrosodiphenylamine is of no interest, the analyst may proceed directly with gas chromatographic analysis (Section 12).

  - Determine   the   original   sample   vol- ume  by  refilling  the  sample  bottle  to  the mark and transferring the liquid to a 1000- mL  graduated  cylinder.  Record  the  sample volume to the nearest 5 mL.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 607

- Cleanup and Separation

  - Cleanup procedures may not be nec- essary for a  relatively  clean  sample  matrix. If particular circumstances demand  the  use of a cleanup procedure, the analyst may use either procedure below  or any other  appro- priate procedure. However, the analyst first must demonstrate that the requirements of Section 8.2 can be met using the method as revised to incorporate the cleanup  proce- dure. Diphenylamine, if present in the origi- nal sample extract, must be separated  from the nitrosamines if  N-nitrosodiphenylamine is to be determined by this method.

  - If the entire extract is  to  be  cleaned up by one of the following procedures, it must be concentrated to 2.0 mL. To the con- centrator tube in Section 10.7, add a clean boiling chip and attach a two-ball micro- Snyder column. Prewet the column by  add- ing about 0.5 mL of methylene  chloride  to the top. Place the micr-K-D apparatus  on  a hot water bath (60 to 65 C) so that the con- centrator tube is partially immersed in  the hot water. Adjust the vertical position of the apparatus and the water temperature as re- quired to complete the concentration in 5 to 10 min. At the proper rate of distillation the balls of the column will actively  chatter  but the chambers will not flood. When the appar- ent volume of liquid reaches about 0.5 mL, remove the K-D apparatus and allow it to drain and cool for at least  10  min.  Remove the micro-Snyder column and rinse its lower joint into the concentrator tube with 0.2 mL of methylene chloride. Adjust the final vol- ume to 2.0 mL and proceed with one of the following cleanup procedures.

  - Florisil column cleanup for nitrosamines:

    - Place 22  g  of  activated  Florisil  into a 22-mm ID chromatographic column. Tap the column to settle the Florisil and add about 5 mm of anhydrous sodium sulfate to the top.

    - Preelute the  column with  40 mL  of ethyl ether/pentane (15 + 85)(V/V). Discard the eluate and just  prior to exposure of  the sodium sulfate layer to the  air,  quan- titatively transfer the 2-mL sample extract onto the column using an additional 2 mL of pentane to complete the transfer.

    - Elute the column with  90  mL  of ethyl ether/pentane (15 + 85)(V/V) and discard the eluate. This fraction will contain the diphenylamine, if it is present in the extract.

    - Next, elute the column with 100 mL of acetone/ethyl ether (5 + 95)(V/V) into a 500- mL K-D flask equipped with a 10-mL concen- trator tube. This fraction will contain  all  of the nitrosamines listed in the scope of the method.

    - Add 15 mL of methanol to the col- lected fraction and concentrate as in Section 10.6, except use pentane to prewet the col- umn  and  set  the  water  bath  at  70  to  75  C.

When the apparatus is cool, remove  the  Sny- der column and rinse the flask and its lower joint into the concentrator tube with  1  to  2 mL of pentane. Analyze by gas  chroma- tography  (Section  12).

  - Alumina column cleanup for nitrosamines:

    - Place 12 g of the alumina prepara- tion (Section 6.10) into a 10-mm ID chromatographic column. Tap the column to settle the alumina and add 1 to 2 cm of anhy- drous sodium  sulfate  to  the top.

    - Preelute the  column with  10 mL  of ethyl ether/pentane (3 + 7)(V/V). Discard the eluate (about 2 mL) and just prior to expo- sure of the sodium sulfate layer to the air, quantitatively transfer the 2 mL sample ex- tract onto the column using an  additional  2 mL of pentane to complete the transfer.

    - Just prior to exposure of the sodium sulfate layer to the air, add 70 mL of ethyl ether/pentane (3 + 7)(V/V). Discard the first 10 mL of eluate. Collect the remainder of the eluate in a 500–mL K-D flask equipped with a 10 mL concentrator tube. This fraction con- tains N-nitrosodiphenylamine and probably a small amount of N-nitrosodi-n-propylamine.

    - Next, elute the column  with  60  mL of ethyl ether/pentane (1 + 1)(V/V), collecting the eluate in a second K-D flask equipped with a 10–mL concentrator tube. Add 15 mL of methanol to the K-D flask. This  fraction will  contain  N-nitrosodimethylamine,  most of the N-nitrosodi-n-propylamine and any diphenylamine that is present.

    - Concentrate both fractions as in Section 10.6, except use pentane to  prewet the column. When the apparatus is cool, re- move the Snyder column and rinse the  flask and its  lower  joint  into  the  concentrator tube with 1 to 2 mL of pentane. Analyze the fractions  by  gas   chromatography   (Section 12).

- Gas Chromatography

  - N-nitrosodiphenylamine completely reacts to form diphenylamine at the normal operating temperatures of  a  GC  injection port (200 to 250 C). Thus, N- nitrosodiphenylamine is chromatographed and detected as diphenylamine. Accurate de- termination depends on removal of diphenylamine that may be present in the original extract prior to GC analysis (See Section 11).

  - Table 1 summarizes the recommended operating conditions for the gas chro- matograph. Included in this table are reten- tion times and MDL that can be achieved under these conditions. Examples of the sep- arations achieved by Column 1 are shown in Figures 1 and 2. Other packed or capillary (open-tubular) columns, chromatographic conditions, or detectors may be used if the requirements of Section 8.2 are met.

  - Calibrate the system daily as de- scribed in Section 7.

#### Pt. 136, App. A, Meth. 607

  - If the  extract  has not  been  subjected to one of the cleanup procedures  in  Section 11, it is necessary to exchange the solvent from methylene chloride to methanol before the thermionic detector can be used. To a 1 to 10-mL volume of methylene chloride ex- tract in a concentrator tube, add 2 mL of methanol and a clean boiling chip. Attach a two-ball micro-Snyder column to the con- centrator tube. Prewet the column by adding about 0.5 mL of methylene chloride to  the top. Place the micro-K-D apparatus on a boiling (100 C) water bath so that the con- centrator tube is partially immersed in  the hot water. Adjust the vertical position of the apparatus and the water temperature as re- quired to complete the concentration in 5 to 10 min. At the proper rate of distillation the balls of the column will actively  chatter  but the chambers will not flood. When the appar- ent volume of liquid reaches about 0.5 mL, remove the K-D apparatus and allow it to drain and cool for at least  10  min.  Remove the micro-Snyder column and rinse its lower joint into the concentrator tube with 0.2 mL of methanol. Adjust the final volume to  2.0 mL.

  - If the internal standard calibration procedure is being used, the internal stand- ard must be added to the sample extract and mixed thoroughly immediately before injec- tion into the gas chromatograph.

  - Inject  2  to  5  L  of  the  sample  extract

or standard into the gas chromatograph using the solvent-flush technique. 21 Smaller (1.0 L) volumes may be injected if auto- matic devices are employed. Record the vol- ume injected to the nearest 0.05 L, and the resulting peak size in area or peak height units.

  - Identify the parameters in the sample by comparing the retention times of the peaks in the sample chromatogram with those of the peaks in standard chromatograms. The width of the retention time window used to make identifications should be based upon measurements of ac- tual retention time variations of standards over the course of a day. Three times the standard deviation of a retention time for a compound can be used to calculate a sug- gested window size; however, the experience of the analyst should weigh heavily in the interpretation of chromatograms.

  - If the response for a peak exceeds the working range of the system, dilute the ex- tract and reanalyze.

  - If the measurement of the peak re- sponse is prevented by the presence of inter- ferences, further cleanup is required.

- Calculations

  - Determine the concentration of indi- vidual compounds in the sample.

    - If the external standard calibration procedure is used, calculate the amount of material  injected  from  the  peak  response

#### 40 CFR Ch. I (7–1–17 Edition)

using the calibration curve or calibration factor determined in Section 7.2.2. The con- centration in the sample can be calculated from Equation 2.

AVt 

## Concentration (g/L) 

Vi Vs 

Equation   2

where:

A = Amount of material injected (ng). Vi = Volume of extract injected (L). Vt = Volume of total extract (L).

Vs = Volume of water extracted (mL).

    - If the internal standard calibration procedure is used, calculate the concentra- tion in the sample using the response factor (RF) determined in Section 7.3.2 and Equa- tion 3.

As Cis 

## RF 

Ais Cs 

Equation   3

where:

As  = Response for the parameter to be meas- ured.

Ais = Response for the internal standard.

Is   =  Amount  of  internal  standard  added  to each extract (g).

Vo = Volume of water extracted (L).

13.2 Report results in g/L without correc- tion for recovery data. All QC data obtained should be reported with the sample results.

- Method Performance

  - The method detection limit (MDL) is defined as the minimum concentration of a substance that can be measured and reported with 99% confidence that the value is above zero. 3 The MDL concentrations listed  in Table 1 were obtained using reagent water. 22 Similar results were achieved using rep- resentative wastewaters. The MDL actually achieved in a given analysis will vary de- pending on instrument sensitivity and ma- trix  effects.

  - This method has been tested for lin- earity of spike recovery from reagent water and has been demonstrated to be applicable over the concentration range from 4 MDL to 1000 MDL. 22

  - This method was tested by 17 labora- tories using reagent water, drinking water, surface water, and three industrial wastewaters spiked at six concentrations over the range 0.8 to 55 g/L. 23 Single oper- ator precision, overall precision, and method accuracy were found to be directly related to the concentration of the parameter and es- sentially independent of the sample matrix. Linear equations to describe these relation- ships are presented in Table 3.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 607

References

    - Fine, D.H., Lieb, D., and Rufeh, R. ‘‘Principle of Operation of the Thermal En- ergy Analyzer for the Trace Analysis of Volatile and Non-volatile N-nitroso Com- pounds,’’ Journal of Chromatography, 107, 351 (1975).

    - Fine, D.H., Hoffman, F., Rounbehler, D.P., and Belcher, N.M. ‘‘Analysis of N-nitro- so Compounds by Combined High Perform- ance Liquid Chromatography and Thermal Energy  Analysis,’’  Walker,  E.A.,  Bogovski,

P. and  Griciute, L., Editors, N-nitroso Com- pounds—Analysis and Formation, Lyon, International Agency for Research on Cancer (IARC Scientific Publications No.  14),  pp.  43– 50 (1976).

    - 40 CFR part 136, appendix B.

    - ‘‘Determination of Nitrosamines in In- dustrial and Municipal Wastewaters,’’ EPA 600/4–82–016, National Technical Information Service, PB82–199621, Springfield, Virginia 22161, April 1982.

    - ASTM Annual Book of Standards, Part 31, D3694–78. ‘‘Standard Practices for Prepa- ration of Sample Containers and for Preser- vation of Organic Constituents,’’ American Society for Testing and Materials, Philadel- phia.

    - Buglass, A.J., Challis, B.C., and Osborn,

M.R.  ‘‘Transnitrosation  and  Decomposition of Nitrosamines,’’ Bogovski, P. and Walker, E.A., Editors, N-nitroso Compounds in the Environment,  Lyon,  International   Agency for Research on Cancer (IARC Scientific Publication No. 9), pp. 94–100 (1974).

    - Burgess, E.M., and Lavanish, J.M. ‘‘Pho- tochemical	Decomposition	of	N- nitrosamines,’’ Tetrahedon Letters, 1221 (1964)

    - Druckrey, H.,  Preussmann,  R., Ivankovic, S., and Schmahl, D. ‘‘Organotrope Carcinogene Wirkungen bei 65 Verschiedenen N-NitrosoVerbindungen an BD-Ratten,’’ Z. Krebsforsch., 69, 103 (1967).

    - Fiddler, W. ‘‘The Occurrence and Deter- mination of N-nitroso Compounds,’’ Toxicol. Appl. Pharmacol., 31, 352 (1975).

    - ‘‘Carcinogens—Working With Carcino- gens,’’ Department of Health, Education, and Welfare, Public Health Service, Center for Disease Control, National Institute for Occu- pational Safety and Health, Publication No. 77–206, August 1977.

    - ‘‘OSHA Safety and Health Standards, General Industry,’’ (29 CFR Part 1910), Occu- pational Safety and Health Administration, OSHA 2206 (Revised, January 1976).

    - ‘‘Safety in Academic Chemistry Labora- tories,’’ American Chemical Society Publica- tion, Committee on Chemical Safety, 3rd Edition, 1979.

    - Lijinsky, W. ‘‘How Nitrosamines Cause Cancer,’’ New Scientist, 73, 216 (1977).

    - Mirvish, S.S. ‘‘N-Nitroso compounds: Their Chemical and in vivo Formation and Possible Importance as Environmental Car- cinogens,’’ J. Toxicol. Environ. Health, 3, 1267 (1977).

    - ‘‘Reconnaissance of Environmental Lev- els of  Nitrosamines in  the  Central United States,’’ EPA–330/1–77–001, National Enforce- ment Investigations Center, U.S. Environ- mental Protection Agency (1977).

    - ‘‘Atmospheric Nitrosamine Assessment Report,’’ Office of Air Quality Planning and Standards, U.S. Environmental Protection Agency, Research Triangle  Park, North Carolina (1976).

    - ‘‘Scientific and Technical Assessment Report on Nitrosamines,’’ EPA–660/6–7–001, Office of Research and Development, U.S. Environmental Protection Agency (1976).

    - Provost,   L.P.,  and   Elder,   R.S.  ‘‘Inter- pretation  of  Percent  Recovery  Data,’’  Amer- ican Laboratory, 15, 58–63 (1983). (The value

2.44 used in the equation in Section 8.3.3 is two times the value of 1.22 derived in this re- port.)

    - ASTM Annual Book of Standards, Part 31, D3370–76. ‘‘Standard Practices for Sam- pling Water,’’ American Society for Testing and  Materials,  Philadelphia.

    - ‘‘Methods 330.4 (Titrimetric, DPD-FAS) and 330.5 (Spectrophotometric, DPD) for Chlorine, Total Residual,’’ Methods for Chemical Analysis of Water and Wastes, EPA–600/4–79–020, U.S. Environmental Pro- tection Agency, Environmental Monitoring and Support Laboratory, Cincinnati, Ohio 45268, March 1979.

    - Burke, J. A. ‘‘Gas Chromatography for Pesticide Residue Analysis; Some Practical Aspects,’’ Journal of the Association of Official Analytical Chemists, 48, 1037 (1965).

    - ‘‘Method Detection Limit  and  Analyt- ical Curve Studies EPA Methods 606, 607, and 608,’’ Special letter report for EPA Contract 68–03–2606, U.S. Environmental Protection Agency, Environmental Monitoring and Sup- port  Laboratory,  Cincinnati,  Ohio  45268, June 1980.

    - ‘‘EPA Method Study 17 Method 607— Nitrosamines,’’ EPA 600/4–84–051, National Technical Information Service, PB84–207646, Springfield, Virginia 22161, June 1984.

TABLE 1—CHROMATOGRAPHIC CONDITIONS AND METHOD DETECTION LIMITS

| Parameter | Retention time (min) | Method de- tection limit (g/L) |
| --- | --- | --- |
|  | Column 1 | Column 2 |  |
| N-Nitrosodimethylamine ................................................................................................ N-Nitrosodi-n-propylamine ............................................................................................. | 4.1 12.1 | 0.88 4.2 | 0.15 .46 |

#### Pt. 136, App. A, Meth. 607

40 CFR Ch. I (7–1–17 Edition)

TABLE 1—CHROMATOGRAPHIC CONDITIONS AND METHOD DETECTION LIMITS—Continued

| Parameter | Retention time (min) | Method de- tection limit (g/L) |
| --- | --- | --- |
|  | Column 1 | Column 2 |  |
| N-Nitrosodiphenylamine a .............................................................................................. | b 12.8 | c 6.4 | .81 |

Column 1 conditions: Chromosorb W-AW (80/100 mesh) coated with 10% Carbowax 20 M/2% KOH packed in a 1.8 m long  4mm ID glass column with helium carrier gas at 40 mL/min flow rate. Column temperature held isothermal at 110 C, except where otherwise indicated.

Column 2 conditions: Supelcoport (100/120 mesh) coated with 10% SP–2250 packed in a 1.8 m long 4 mm ID glass column with helium carrier gas at 40 mL/min flow rate. Column temperature held isothermal at 120 C, except where otherwise indicated.

a Measured as diphenylamine. b 220 C column temperature. c 210 C column temperature.

TABLE 2—QC ACCEPTANCE CRITERIA—METHOD 607

| Parameter | Test conc. (g/L) | Limit for s (g/L) | Range for X¯ (g/L) | Range for P, Ps (per- cent) |
| --- | --- | --- | --- | --- |
| N-Nitrosodimethylamine ........................................................................ | 20 | 3.4 | 4.6–20.0 | 13–109 |
| N-Nitrosodiphenyl .................................................................................. | 20 | 6.1 | 2.1–24.5 | D–139 |
| N-Nitrosodi-n-propylamine .................................................................... | 20 | 5.7 | 11.5–26.8 | 45–146 |

s = Standard deviation for four recovery measurements, in g/L (Section 8.2.4). X¯ = Average recovery for four recovery measurements, in g/L (Section 8.2.4).

P, Ps  = Percent recovery measured (Section 8.3.2, Section 8.4.2). D = Detected; result must be greater than zero.

NOTE: These criteria are based directly upon the method performance data in Table 3. Where necessary, the limits for recov- ery have been broadened to assure applicability of the limits to concentrations below those used to develop Table 3.

TABLE 3—METHOD ACCURACY AND PRECISION AS FUNCTIONS OF CONCENTRATION—METHOD 607

| Parameter | Accuracy, as recovery, X (g/L) | Single analyst precision, sr (g/L) | Overall preci- sion, S(g/L) |
| --- | --- | --- | --- |
| N-Nitrosodimethylamine .................................................................................... | 0.37C + 0.06 | 0.25X¯ ¥0.04 | 0.25X¯ + 0.11 |
| N-Nitrosodiphenylamine .................................................................................... | 0.64C + 0.52 | 0.36X¯ ¥1.53 | 0.46X¯ ¥0.47 |
| N-Nitrosodi-n-propylamine ................................................................................. | 0.96C¥0.07 | 0.15X¯ + 0.13 | 0.21X¯ + 0.15 |

X= Expected recovery for one or more measurements of a sample containing a concentration of C, in g/L.

sr= Expected single analyst standard deviation of measurements at an average concentration found of X¯ , in g/L. S= Expected interlaboratory standard deviation of measurements at an average concentration found of X¯ , in g/L. C = True value for the concentration, in g/L.

X¯ = Average recovery found for measurements of samples containing a concentration of C, in g/L.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 607

Pt. 136, App. A, Meth. 607

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 608

METHOD 608—ORGANOCHLORINE PESTICIDES AND PCBS

- Scope and Application

| Parameter | STORET No. | CAS No. |
| --- | --- | --- |
| Aldrin ...................................... | 39330 | 309–00–2 |
| a–BHC ................................... | 39337 | 319–84–6 |
| b–BHC ................................... | 39338 | 319–85–7 |
| d–BHC ................................... | 34259 | 319–86–8 |
| g–BHC .................................... | 39340 | 58–89–9 |
| Chlordane .............................. | 39350 | 57–74–9 |
| 4,4–DDD ............................... | 39310 | 72–54–8 |
| 4,4–DDE ............................... | 39320 | 72–55–9 |
| 4,4–DDT ............................... | 39300 | 50–29–3 |
| Dieldrin ................................... | 39380 | 60–57–1 |
| Endosulfan I .......................... | 34361 | 959–98–8 |
| Endosulfan II ......................... | 34356 | 33212–65–9 |
| Endosulfan sulfate ................. | 34351 | 1031–07–8 |
| Eldrin ...................................... | 39390 | 72–20–8 |
| Endrin aldehyde ..................... | 34366 | 7421–93–4 |
| Heptachlor ............................. | 39410 | 76–44–8 |
| Heptachlor epoxide ................ | 39420 | 1024–57–3 |
| Toxaphene ............................. | 39400 | 8001–35–2 |
| PCB–1016 ............................. | 34671 | 12674–11–2 |
| PCB–1221 ............................. | 39488 | 1104–28–2 |
| PCB–1232 ............................. | 39492 | 11141–16–5 |
| PCB–1242 ............................. | 39496 | 53469–21–9 |
| PCB–1248 ............................. | 39500 | 12672–29–6 |
| PCB–1254 ............................. | 39504 | 11097–69–1 |
| PCB–1260 ............................. | 39508 | 11096–82–5 |

1.1 This method covers the determination of certain organochlorine  pesticides  and PCBs. The following parameters can be de- termined by this method:

procedures. The analyst is allowed the lati- tude, under Section 12, to select chromatographic conditions appropriate for the simultaneous measurement of combina- tions of these parameters.

  - Any modification of this method,  be- yond those expressly permitted, shall be con- sidered as a major modification subject to application and approval of alternate test procedures under 40 CFR 136.4 and 136.5.

  - This method is restricted to use by or under the supervision of analysts experi- enced in the use of a gas chromatograph and in the interpretation of gas chromatograms. Each analyst must demonstrate  the  ability to generate acceptable results with this method using the procedure described in Sec- tion 8.2.

  - This is a gas chromatographic (GC) method  applicable  to  the  determination  of the compounds listed above in municipal and industrial discharges as  provided  under  40 CFR 136.1. When this method is used to  ana- lyze unfamiliar samples for any or all of the compounds above, compound identifications should be supported by  at  least  one  addi- tional qualitative technique. This method describes  analytical  conditions  for  a  second gas  chromatographic  column  that   can   be used  to  confirm  measurements  made  with the primary column. Method 625 provides gas chromatograph/mass spectrometer (GC/MS) conditions  appropriate  for   the   qualitative and  quantitative  confirmation  of  results   for all of the parameters listed above, using the extract  produced  by  this  method.

  - The method detection limit (MDL, de- fined in Section 14.1) 1 for each parameter is listed in Table 1. The MDL for a specific wastewater may differ from those listed, de- pending upon the nature of interferences  in the sample matrix.

  - The sample extraction and concentra- tion steps in this method are essentially the same as in Methods 606, 609, 611, and 612. Thus, a single sample may be extracted to measure the parameters included in the scope of each of these methods. When clean- up is required, the concentration levels must be high  enough  to  permit  selecting  aliquots, as  necessary,  to  apply  appropriate  cleanup

- Summary of Method

  - A measured volume of sample, ap- proximately 1–L, is extracted with  meth- ylene chloride using a separatory funnel. The methylene chloride extract is dried and ex- changed to hexane during concentration to a volume of 10 mL or less. The extract is sepa- rated by gas chromatography and the param- eters are then measured with an electron capture detector. 2

  - The method provides a Florisil column cleanup procedure and an elemental sulfur removal procedure to aid  in  the  elimination of interferences that may be encountered.

- Interferences

  - Method interferences may be caused by contaminants in solvents, reagents, glass- ware, and other sample processing hardware that lead to discrete artifacts and/or ele- vated baselines in gas chromatograms. All of these materials must be routinely dem- onstrated to be free from interferences under the conditions of the analysis by running laboratory reagent blanks as described in Section 8.1.3.

    - Glassware must be scrupulously cleaned. 3 Clean all glassware as soon as pos- sible after use by rinsing with the last sol- vent used in it. Solvent rinsing should be fol- lowed by detergent washing with hot water, and rinses with tap water and distilled water. The glassware should then be drained dry, and heated in a muffle furnace at 400 C for 15 to 30 min. Some thermally stable ma- terials, such as PCBs, may not be eliminated by this treatment. Solvent rinses with ace- tone and pesticide quality hexane may be substituted for the muffle furnace heating. Thorough rinsing with such solvents usually eliminates PCB interference. Volumetric ware should not be heated in a muffle fur- nace. After drying and cooling, glassware should be sealed and stored in a clean envi- ronment to prevent any accumulation of dust or other contaminants. Store inverted or capped with aluminum foil.

#### Pt. 136, App. A, Meth. 608

    - The use of high purity reagents and solvents helps to minimize interference prob- lems. Purification of solvents  by  distillation in all-glass systems may be required.

  - Interferences by phthalate esters can pose a major problem in pesticide analysis when using the electron capture detector. These compounds generally appear in the chromatogram as large late eluting peaks, especially in the 15 and 50% fractions from Florisil. Common flexible plastics contain varying amounts of phthalates. These phthalates are  easily  extracted or  leached from such materials during laboratory oper- ations. Cross contamination of clean glass- ware routinely occurs when plastics are han- dled during extraction steps, especially when solvent-wetted surfaces are handled. Inter- ferences from phthalates can best be mini- mized by avoiding the use of plastics in the laboratory. Exhaustive  cleanup of  reagents and glassware may be required to eliminate background phthalate contamination. 4 5 The interferences from phthalate esters can be avoided by using a microcoulometric or elec- trolytic   conductivity   detector.

  - Matrix interferences may be caused by contaminants that are co-extracted from the sample. The extent of matrix interferences will vary considerably from source to source, depending upon the nature and diversity  of the industrial complex or municipality being sampled.  The  cleanup  procedures  in  Section

11 can be used to overcome many of these interferences, but unique samples may re- quire additional cleanup approaches to achieve the MDL listed in Table 1.

- Safety

  - The   toxicity   or   carcinogenicity   of each  reagent  used  in  this  method  has  not been precisely defined; however, each chem- ical compound should be treated as a poten- tial health hazard. From this viewpoint, ex- posure to these chemicals must be reduced to the lowest possible level by whatever means available. The laboratory is responsible for maintaining   a   current   awareness   file   of OSHA  regulations  regarding  the  safe  han- dling of the chemicals specified in this meth- od. A reference file of material data handling sheets should also be made available to all personnel involved in the chemical analysis. Additional  references  to  laboratory  safety are available and have been identified 6M8 for the information of the analyst.

  - The following parameters covered by this method have been tentatively classified as known or suspected, human or mamma- lian carcinogens: 4,4-DDT, 4,4–DDD, the BHCs, and the PCBs. Primary standards of these toxic compounds should be prepared in a hood. A NIOSH/MESA approved toxic gas respirator should be worn when the analyst handles high concentrations of these toxic compounds.

#### 40 CFR Ch. I (7–1–17 Edition)

- Apparatus and Materials

  - Sampling equipment, for discrete or composite  sampling.

    - Grab sample bottle—1–L or 1-qt, amber glass, fitted with a screw cap lined with Teflon. Foil may be substituted for Tef- lon if the sample is not corrosive. If amber bottles are not available, protect samples from light. The bottle and cap liner must be washed, rinsed with acetone or methylene chloride, and dried before use to minimize contamination.

    - Automatic sampler (optional)—The sampler must incorporate glass sample con- tainers for the collection of a minimum of 250 mL of sample. Sample containers must be kept refrigerated at 4 C and protected from light during composting. If the sampler uses a peristaltic pump, a minimum length of compressible silicone rubber tubing may be used. Before use, however, the compressible tubing should be thoroughly rinsed with methanol, followed by repeated rinsings with distilled water to minimize the potential for contamination of the sample. An integrating flow meter is required to collect flow propor- tional  composites.

  - Glassware (All specifications are sug- gested. Catalog numbers are included for il- lustration only.):

    - Separatory funnel—2–L, with Teflon stopcock.

    - Drying column—Chromatographic column, approximately 400 mm long 19 mm ID,  with  coarse  frit  filter  disc.

    - Chromatographic column—400 mm long 22 mm ID, with Teflon stopcock and coarse frit filter disc (Kontes K–42054 or equivalent).

    - Concentrator tube, Kuderna-Dan- ish—10–mL, graduated (Kontes K–570050–1025 or equivalent). Calibration must  be  checked at the volumes employed in the test. Ground glass stopper is used to prevent evaporation of  extracts.

    - Evaporative flask, Kuderna-Danish— 500–mL (Kontes K–570001–0500 or equivalent). Attach  to  concentrator  tube  with  springs.

    - Snyder column, Kuderna/Danish— Three-ball macro (Kontes K–503000–0121 or equivalent).

    - Vials—10 to 15–mL, amber glass, with Teflon-lined screw cap.

  - Boiling chips—Approximately 10/40 mesh. Heat to 400 C for 30 min or Soxhlet ex- tract  with  methylene  chloride.

  - Water bath—Heated, with concentric ring cover, capable of temperature control (2 C). The bath should be used in a hood.

  - Balance—Analytical, capable of accu- rately weighing 0.0001 g.

  - Gas chromatograph—An analytical system complete with gas chromatograph suitable for on-column injection and all re- quired accessories including syringes, ana- lytical columns, gases, detector, and strip-

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 608

chart recorder. A data system is rec- ommended for measuring peak areas.

    - Column  1—1.8  m  long  4  mm  ID

glass, packed with 1.5% SP–2250/1.95% SP– 2401 on Supelcoport (100/120 mesh) or equiva- lent. This column was used to develop the method   performance   statements   in   Section

- Guidelines for the use of alternate col- umn packings are provided in Section 12.1.

    - Column  2—1.8  m  long  4  mm  ID

glass, packed with 3% OV–1 on Supelcoport (100/120 mesh) or equivalent.

    - Detector—Electron capture detector. This detector has proven effective in the analysis of wastewaters for the parameters listed in the scope (Section 1.1), and was used to develop the method performance state- ments in Section 14. Guidelines for the use of alternate detectors are provided in Section 12.1.

  - Reagents

  - Reagent water—Reagent water is de- fined as a water in which  an  interferent  is not observed at the  MDL  of  the  parameters of  interest.

  - Sodium hydroxide solution (10 N)— Dissolve 40 g of NaOH (ACS) in reagent water and dilute to 100 mL.

  - Sodium thiosulfate—(ACS) Granular.

  - Sulfuric acid (1 + 1)—Slowly, add  50 mL to H2SO4 (ACS, sp. gr. 1.84) to 50 mL of reagent water.

  - Acetone, hexane, isooctane, methylene chloride—Pesticide quality or equivalent.

  - Ethyl ether—Nanograde, redistilled in glass if necessary.

    - Ethyl ether must be shown to be free of peroxides before it is used as indicated by EM Laboratories Quant  test  strips.  (Avail- able from Scientific Products Co., Cat. No. P1126–8, and other suppliers.)

    - Procedures recommended for re- moval of peroxides are provided with the test strips. After cleanup, 20 mL of ethyl alcohol preservative must be added to each liter of ether.

  - Sodium sulfate—(ACS) Granular, an- hydrous. Purify by heating at 400 C for 4 h in a shallow tray.

  - Florisil—PR grade (60/100 mesh). Pur- chase activated at 1250 F and store in the dark in glass containers with ground glass stoppers or foil-lined screw caps. Before use, activate each batch at least 16 h at 130 C in a foil-covered glass container and allow to cool.

  - Mercury—Triple  distilled.

  - Copper powder—Activated.

  - Stock    standard    solutions    (1.00    g/

L)—Stock standard solutions can be pre- pared from pure standard materials or pur- chased as certified solutions.

    - Prepare stock standard solutions by accurately weighing about 0.0100 g of pure material. Dissolve  the  material  in  isooctane and  dilute  to  volume  in  a  10-mL  volumetric

flask. Larger volumes can be used at the con- venience of the analyst. When compound pu- rity is assayed to be 96% or greater, the weight can be used without correction to cal- culate the concentration of the stock stand- ard. Commercially prepared stock standards can be used at any concentration if they are certified by the manufacturer or by an inde- pendent source.

    - Transfer the stock standard solu- tions into Teflon-sealed screw-cap bottles. Store at 4 C and protect from light. Stock standard solutions should be checked fre- quently for signs of degradation or evapo- ration, especially just prior to preparing calibration standards from them.

    - Stock standard solutions must be replaced after six months, or sooner if com- parison with check standards indicates a problem.

6.12 Quality control check sample con- centrate—See Section 8.2.1.

  - Calibration

  - Establish gas chromatographic oper- ating conditions equivalent to those given in Table 1. The gas chromatographic system can be calibrated using the external standard technique (Section 7.2) or the internal stand- ard technique (Section 7.3).

  - External standard calibration proce- dure:

    - Prepare calibration standards at a minimum of three concentration levels  for each parameter of interest by adding vol- umes of one or more stock standards to a volumetric flask and diluting to volume with isooctane. One of the external standards should be at a concentration near, but above, the MDL (Table 1) and the other concentra- tions should correspond to the expected range of concentrations found in real sam- ples or should define the working range of the detector.

    - Using injections of 2 to 5 L, analyze each calibration standard according to Sec- tion 12 and tabulate peak height or area re- sponses against the mass injected. The re- sults can be used to prepare a calibration curve for each compound. Alternatively, if the ratio of response to amount injected (calibration factor) is a constant over the working range (<10% relative standard devi- ation, RSD), linearity through the origin can be assumed and the average ratio or calibra- tion factor can be used in place of a calibra- tion  curve.

  - Internal standard calibration proce- dure—To use this approach, the analyst must select one or more internal standards that are similar in analytical behavior to the compounds of interest. The analyst must fur- ther demonstrate that the measurement of the internal standard is not affected by method or matrix interferences. Because of these  limitations,  no  internal  standard  can

#### Pt. 136, App. A, Meth. 608

be suggested that is applicable to all sam- ples.

    - Prepare calibration standards at a minimum of three concentration levels  for each parameter of interest by adding vol- umes of one or more stock standards to a volumetric flask. To each calibration stand- ard, add a known constant amount of one or more internal standards, and dilute to vol- ume with isooctane. One of the standards should be at a concentration near, but above, the MDL and the other concentrations should correspond to the expected range of concentrations found in real samples or should define the working range of the detec- tor.

    - Using injections of 2 to 5 L, analyze

each calibration standard according to Sec- tion 12 and tabulate peak height or area re- sponses against concentration for each com- pound and internal standard. Calculate re- sponse factors (RF) for each compound using Equation 1.

As Cis 

#### 40 CFR Ch. I (7–1–17 Edition)

tion standards through the procedure to vali- date elution patterns and the absence of interferences from the reagents.

  - Quality Control

  - Each laboratory that uses this method is required to operate a formal quality  con- trol program. The minimum requirements of this program consist of an initial demonstra- tion of laboratory capability and an ongoing analysis of spiked samples to evaluate and document data quality. The laboratory must maintain records to document the quality of data that is generated. Ongoing data quality checks are compared with established per- formance criteria to determine if the results of analyses meet the performance character- istics of the method. When results of sample spikes indicate atypical method perform- ance, a quality control check  standard  must be analyzed to confirm that the measure- ments were performed in an in-control mode of operation.

    - The analyst must make an initial, one-time,  demonstration  of  the  ability  to

where:

RF 

Ais Cs 

Equation   1

generate acceptable accuracy and precision with this method. This ability is established as described in Section 8.2.

    - In recognition of advances that are

As  = Response for the parameter to be meas- ured.

Ais = Response for the internal standard.

Cis  = Concentration of the internal standard (g/L).

Cs   =  Concentration  of  the  parameter  to  be measured (g/L).

If the RF value over the working range is a constant (<10% RSD), the RF can be as- sumed to be invariant and the average RF can be used for calculations. Alternatively, the results can be used to plot a calibration curve of response ratios, As/Ais, vs. RF.

  - The working calibration curve, cali- bration factor, or RF must be verified on each working day by the measurement of one or more calibration standards. If the re- sponse for any parameter varies from the predicted response by more than 15%, the test must be repeated using a  fresh calibra- tion standard. Alternatively, a new calibra- tion curve must be prepared for that com- pound.

  - The cleanup procedure in Section 11 utilizes Florisil column chromatography. Florisil from different  batches  or  sources may vary in adsorptive capacity. To stand- ardize the amount of Florisil which  is  used, the use of lauric acid value 9 is  suggested. The referenced procedure determines the ad- sorption from hexane solution of lauric  acid (mg) per g of Florisil. The amount of Florisil to be  used  for each  column  is  calculated by dividing 110 by this ratio and multiplying by 20 g.

  - Before using any cleanup procedure, the analyst must process a series of calibra-

occurring in chromatography, the analyst is permitted certain options (detailed in Sec- tions 10.4, 11.1, and 12.1) to improve the sepa- rations or lower the cost of measurements. Each time such a modification is  made  to the method, the analyst is required to repeat the procedure in Section 8.2.

    - Before processing any samples, the analyst must analyze a  reagent  water  blank to demonstrate that interferences from the analytical system and glassware are under control. Each time a set of samples is ex- tracted or reagents are changed, a reagent water blank must be processed as a safe- guard  against  laboratory  contamination.

    - The laboratory must, on an ongoing basis, spike and analyze a minimum of 10% of all samples to monitor and evaluate lab- oratory data quality. This procedure is de- scribed in Section 8.3.

    - The laboratory must, on an ongoing basis, demonstrate through the analyses of quality control  check standards  that  the op- eration of the measurement system is in con- trol.  This  procedure  is  described  in  Section

8.4. The frequency of the check standard analyses is equivalent to 10% of all samples analyzed but may be reduced if spike recov- eries from samples (Section 8.3) meet all specified quality control criteria.

    - The laboratory must maintain per- formance records to document the quality of data that is generated. This procedure is de- scribed in Section 8.5.

  - To establish the ability to generate acceptable accuracy and precision, the ana- lyst must perform the following operations.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 608

    - A quality control (QC) check sample concentrate is required containing each sin- gle-component parameter of interest at the following concentrations in acetone: 4,4– DDD, 10 g/mL; 4,4–DDT, 10 g/mL; endosulfan II, 10 g/mL; endosulfan  sulfate, 10 g/mL; endrin, 10 g/mL; any other single- component pesticide, 2 g/mL. If this method is only to be used to analyze for PCBs, chlordane, or toxaphene, the QC check  sam- ple concentrate should contain the most rep- resentative multicomponent parameter at a concentration of 50 g/mL in acetone. The QC check sample concentrate must be obtained from the U.S. Environmental Protection Agency, Environmental Monitoring and Sup- port Laboratory in Cincinnati, Ohio, if avail- able. If not available from  that  source,  the QC check sample concentrate must be ob- tained from another external source. If not available from either source above, the QC check sample concentrate must be prepared by the laboratory using stock standards pre- pared independently from those used for cali- bration.

    - Using a pipet, prepare QC check sam- ples at the test concentrations  shown  in Table 3 by adding 1.00 mL  of  QC  check  sam- ple concentrate to each  of  four  1–L  aliquots of  reagent  water.

    - Analyze the well-mixed QC check samples according to the  method  beginning in Section 10.

    - Calculate the average recovery (X¯ ) in

g/mL; and the standard deviation of the re- covery (s) in g/mL, for  each  parameter using the four results.

    - For each parameter compare s and X¯

with the corresponding acceptance criteria for   precision   and   accuracy,   respectively,

found in Table 3. If s and X¯  for all param-

eters of interest meet the acceptance cri- teria, the system performance is acceptable and analysis of actual samples can begin. If any individual s exceeds the precision limit

or any individual X¯  falls outside the range

for accuracy, the system performance is un- acceptable for that parameter.

NOTE: The large number of parameters in Table 3 present  a  substantial  probability that one or more will fail at least one of the acceptance criteria when all parameters are analyzed.

    - When one or more of the parameters tested fail at least one of the acceptance cri- teria, the analyst must proceed according to Section 8.2.6.1 or 8.2.6.2.

      - Locate and correct the source of the problem and repeat the test for all pa- rameters of interest beginning with Section 8.2.2.

      - Beginning with Section 8.2.2, repeat the test only for those  parameters  that failed to meet criteria. Repeated failure, however, will confirm a  general  problem with the measurement system. If this occurs, locate and correct the source of the problem

and repeat the test for all compmunds of in- terest beginning with Section 8.2.2.

  - The laboratory must, on an ongoing basis, spike at least 10% of the samples from each sample site being monitored to assess accuracy. For laboratories analyzing one to ten samples per month, at least one spiked sample per month is required.

    - The concentration of the spike in the sample should be determined as follows:

      - If, as in compliance monitoring, the concentration of a specific parameter in the sample is being checked against a regu- latory concentration limit, the spike should be at that limit or 1 to 5 times higher than the background concentration determined in Section 8.3.2, whichever concentration would be larger.

      - If the concentration of a specific parameter in the sample  is  not  being checked against a limit specific to that pa- rameter, the spike should be at the test con- centration in Section 8.2.2 or 1 to 5 times higher than the background concentration determined in Section 8.3.2, whichever con- centration would be larger.

      - If it is impractical to determine background levels before spiking (e.g., max- imum holding times will be exceeded), the spike concentration should be (1) the regu- latory concentration limit, if any; or, if none

(2) the larger of either 5  times  higher  than the expected  background  concentration  or the test concentration in Section 8.2.2.

    - Analyze one sample aliquot to deter- mine the background concentration (B) of each parameter. If necessary, prepare a new QC check sample concentrate (Section 8.2.1) appropriate for the background concentra- tions in the sample. Spike a second sample aliquot with 1.0 mL of the QC check sample concentrate and analyze it to determine the concentration after spiking (A) of each pa- rameter. Calculate each percent recovery (P) as 100(A¥B)%/T, where T is the known true value of the spike.

    - Compare the percent recovery (P) for each parameter with the corresponding QC acceptance criteria found in Table 3. These acceptance criteria were calculated to  in- clude an allowance for error in measurement of both the background and spike concentra- tions, assuming a spike  to  background  ratio of 5:1. This error will be accounted for to the extent that the analyst’s spike to back- ground ratio approaches 5:1. 10 If spiking was performed at a concentration lower than the test concentration in Section 8.2.2, the ana- lyst must use either the QC acceptance cri- teria in Table 3, or optional QC acceptance criteria calculated for the specific spike con- centration. To calculate optional acceptance criteria for the recovery of a parameter: (1) Calculate accuracy (X) using the equation in Table 4, substituting the spike concentration

(T) for C; (2) calculate overall precision (S) using the equation in Table 4, substituting X

#### Pt. 136, App. A, Meth. 608

for X¯ ; (3) calculate the range for recovery at the spike concentration as (100 X/T)2.44(100 S/T)%. 10

    - If any individual P falls outside the designated range for recovery, that param- eter has failed the acceptance criteria. A check standard containing each parameter that failed the criteria must be analyzed as described in Section 8.4.

  - If any parameter fails the acceptance criteria for recovery in Section 8.3, a QC check standard containing each parameter that failed must be prepared and analyzed.

NOTE: The frequency for the required anal- ysis of a QC check standard will depend upon the number of parameters being simulta- neously tested, the complexity of the sample matrix, and the performance of the labora- tory. If the entire list of parameters in Table 3 must be measured in the sample in Section 8.3, the probability that the analysis of a QC check standard will be required is high.  In this case the QC check standard should be routinely analyzed with the spike sample.

    - Prepare the QC check standard by adding 1.0 mL of QC check sample con- centrate (Section 8.2.1 or 8.3.2) to 1 L of rea- gent water. The QC check standard needs only to contain the parameters that failed criteria in the test in Section 8.3.

    - Analyze the QC check standards to determine the concentration measured (A) of each parameter. Calculate each percent re- covery (Ps) as 100 (A/T)%, where T is the true value of the standard concentration.

    - Compare the percent recovery (Ps) for each parameter with the corresponding QC acceptance criteria found in Table 3. Only parameters that failed the test in Section 8.3 need to be compared with these  criteria.  If the recovery of any such parameter falls out- side the designated range, the laboratory performance for that parameter is judged to be out of control, and the problem must be immediately identified and corrected. The analytical result for that parameter in the unspiked sample is suspect  and may not  be reported for regulatory compliance purposes.

  - As part of the QC program for the lab- oratory, method accuracy for wastewater samples must be assessed and records must be maintained. After the analysis of five spiked wastewater samples as in Section 8.3,

calculate  the  average  percent  recovery  (P¯ )

and the standard deviation of the percent re- covery (sp). Express the accuracy assessment

as a percent recovery interval from P¯ ¥2 sp  to P¯ + 2 sp. If P¯ = 90% and sp = 10%, for example,

the accuracy interval is expressed as 70– 110%. Update the accuracy  assessment  for each parameter on a regular basis (e.g. after each five to  ten  new  accuracy  measure- ments).

  - It is recommended that the laboratory adopt additional quality assurance practices for use with this method. The specific prac- tices that are most productive depend upon

#### 40 CFR Ch. I (7–1–17 Edition)

the needs of the laboratory and the nature of the samples. Field duplicates may be ana- lyzed to assess the precision of the environ- mental measurements. When doubt exists over the identification of a peak on the chro- matogram, confirmatory techniques such as gas chromatography with a dissimilar col- umn, specific element detector, or mass spectrometer must be used. Whenever pos- sible, the laboratory should analyze standard reference materials and participate in rel- evant performance evaluation studies.

  - Sample Collection, Preservation, and Handling

  - Grab samples must be collected  in glass containers. Conventional sampling practices 11 should be followed, except that the bottle must not be prerinsed with sample before collection. Composite samples should be collected in refrigerated  glass  containers in accordance with the requirements of the program. Automatic sampling equipment must be as free as possible of Tygon tubing and other potential sources of contamina- tion.

  - All samples must be iced or refrig- erated  at  4  C  from  the  time  of  collection until extraction. If  the samples  will not  be extracted within 72 h of collection,  the  sam- ple should be adjusted to a pH range of 5.0 to

9.0 with sodium hydroxide solution or sul- furic acid. Record the volume of acid or base used. If aldrin is to be determined, add so- dium thiosulfate when residual chlorine is present. EPA Methods 330.4 and 330.5 may be used for measurement of residual chlorine. 12 Field test kits are available for this purpose.

9.3 All samples must be extracted within 7 days of collection and completely analyzed within 40 days of extraction. 2

  - Sample Extraction

  - Mark the water meniscus on the side of the sample bottle for later determination of sample volume. Pour the entire sample into a 2–L separatory funnel.

  - Add 60 mL of methylene chloride  to the sample bottle, seal, and shake 30 s to rinse the inner surface. Transfer the solvent to the separatory funnel and extract the sample by shaking the funnel for 2 min. with periodic venting to release excess pressure. Allow the organic layer to separate from the water phase for a minimum of 10 min. If the emulsion interface between layers is more than one-third the volume of  the  solvent layer, the analyst must employ mechanical techniques to complete the phase separation. The optium technique depends upon the sam- ple,  but  may  include  stirring,  filtration   of the emulsion through glass wool, centrifuga- tion, or other physical methods. Collect the methylene chloride extract in a 250–mL Er- lenmeyer  flask.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 608

  - Add a second 60-mL volume of meth- ylene chloride to the sample bottle and re- peat the extraction procedure a second time, combining the extracts in the Erlenmeyer flask. Perform a third extraction in the same manner.

  - Assemble a Kuderna-Danish (K-D) concentrator by attaching a 10-mL concen- trator tube to a 500-mL evaporative flask. Other concentration devices or  techniques may be used in place of the K-D concentrator if the requirements of Section 8.2 are met.

  - Pour the combined extract through a solvent-rinsed drying column containing about 10 cm of anhydrous sodium sulfate, and collect the extract in the K-D concen- trator. Rinse the Erlenmeyer flask and col- umn with 20 to 30 mL of methylene chloride to complete the quantitative transfer.

  - Add one or two clean boiling chips to the evaporative flask and attach a three-ball Snyder column. Prewet the Snyder  column by adding about 1 mL of methylene chloride to the top. Place the K-D apparatus on a hot water bath (60 to 65 C) so that the concen- trator tube is partially immersed in the hot water, and the entire lower rounded surface of the flask is bathed with hot vapor. Adjust the vertical position of the apparatus  and the water temperature as required to com- plete the concentration in 15 to  20  min.  At the proper rate of distillation the balls of the column will actively chatter but the cham- bers will not flood with condensed solvent. When the apparent volume of liquid reaches 1 mL, remove the K-D apparatus and allow it to drain and cool for at least 10 min.

  - Increase the temperature of the hot water bath to about 80 C. Momeltarily re- move the Snyder column, add 50 mL  of hexane and a new boiling chip,  and  reattach the  Snyder  column.  Concentrate   the   extract as in Section 10.6, except use hexane  to prewet the column. The elapsed time of con- centration should be 5 to 10 min.

  - Remove the Snyder column and rinse the flask and its lower joint into the concen- trator tube with 1 to 2 mL of hexane. A 5-mL syringe is recommended for this operation. Stopper the concentrator tube and store re- frigerated if further processing will not be performed immediately. If the extract  will be stored longer than two days, it should be transferred to a Teflon-sealed screw-cap vial. If the sample extract requires no further cleanup, proceed with gas chromatographic analysis (Section 12). If the sample requires further cleanup, proceed to Section 11.

  - Determine the original sample vol- ume by refilling the sample bottle to the mark and transferring the liquid to  a  1000- mL graduated cylinder. Record the sample volume to the nearest 5 mL.

  - Cleanup and Separation

  - Cleanup procedures may not be nec- essary  for  a  relatively  clean  sample  matrix.

If particular circumstances demand  the  use of a cleanup procedure, the analyst may use either procedure below  or any other  appro- priate procedure. However, the analyst first must demonstrate that the requirements of Section 8.2 can be met using the method as revised to incorporate the cleanup  proce- dure. The Florisil column allows for a select fractionation of the compounds and will eliminate polar interferences. Elemental sul- fur, which interferes with the electron cap- ture gas chromatography of certain pes- ticides, can be removed by the technique de- scribed in Section 11.3.

  - Florisil column cleanup:

    - Place a weight of Florisil  (nomi- nally 20 g) predetermined by calibration (Section 7.5), into a chromatographic  col- umn. Tap the column to settle the  Florisil and add 1 to 2 cm of anhydrous sodium sul- fate to the top.

    - Add 60 mL of hexane to wet and rinse the sodium sulfate and Florisil. Just prior to exposure of the sodium sulfate layer to the air, stop the elution of the hexane by closing the stopcock on the chromatographic column. Discard the eluate.

    - Adjust  the  sample  extract   volume to 10 mL with hexane and  transfer  it  from the K-D concentrator tube onto the column. Rinse the tube twice with 1 to 2 mL of hexane, adding each rinse to the column.

    - Place a 500-mL K-D flask and clean concentrator	tube	under	the chromatographic column. Drain the column into the flask  until  the  sodium  sulfate  layer is nearly exposed. Elute the column with 200 mL of 6% ethyl ether in hexane (V/V) (Frac- tion 1) at a rate of about 5 mL/min. Remove the K-D flask and set it aside for later con- centration.   Elute   the   column   again,   using

200 mL of 15% ethyl ether in hexane (V/V) (Fraction 2), into a second K-D flask. Per- form the third elution using 200 mL of 50% ethyl ether in hexane (V/V) (Fraction 3). The elution patterns for the pesticides and PCBs are shown in Table 2.

    - Concentrate the fractions as in Sec- tion 10.6, except use hexane to prewet the column  and  set  the  water  bath  at  about  85

C. When the apparatus is cool, remove the Snyder column and rinse  the  flask  and  its lower joint into the concentrator tube with hexane.  Adjust  the  volume   of   each   fraction to 10 mL with hexane and analyze by gas chromatography  (Section  12).

11.3 Elemental sulfur will usually elute entirely in Fraction 1 of the Florisil column cleanup. To remove sulfur interference from this  fraction  or  the  original  extract,  pipet

1.00 mL of the concentrated extract into a clean concentrator tube or  Teflon-sealed vial. Add one to three drops of mercury and seal. 13 Agitate the contents of the vial for 15 to 30 s. Prolonged shaking (2 h) may be re- quired. If so, this may be accomplished with a  reciprocal  shaker.  Alternatively,  activated

#### Pt. 136, App. A, Meth. 608

40 CFR Ch. I (7–1–17 Edition)

copper  powder  may  be  used  for  sulfur  re- moval. 14  Analyze by gas chromatography.

where:

Equation   2

  - Gas Chromatography

  - Table 1 summarizes the recommended operating conditions for the gas chro- matograph. Included in this table are reten- tion times and MDL that can be achieved under these conditions. Examples of the sep- arations achieved by Column 1 are shown in Figures 1 to 10. Other packed or capillary (open-tubular) columns, chromatographic conditions, or detectors may be used if the requirements of Section 8.2 are met.

  - Calibrate the system daily as de- scribed in Section 7.

  - If the internal standard calibration procedure is being used, the internal stand- ard must be added to the sample extract and mixed thoroughly immediately before injec- tion into the gas chromatograph.

  - Inject 2 to 5  L  of  the  sample  extract or  standard  into  the  gas   chromatograph using the solvent-flush  technique. 15  Smaller (1.0 uL) volumes may  be  injected  if  auto- matic devices are employed. Record the vol- ume injected to the nearest 0.05 L, the total extract volume, and the  resulting  peak  size in  area  or  peak  height  units.

  - Identify the parameters in the sample by comparing the retention times of the peaks in the sample chromatogram with those of the peaks in standard chromatograms. The width of the retention time window used to make identifications should be based upon measurements of ac- tual retention time variations of standards over the course of a day. Three times the standard deviation of a retention time for a compound can be used to calculate a sug- gested window size; however, the experience of the analyst should weigh heavily in the interpretation of chromatograms.

  - If the response for a peak exceeds the working range of the system, dilute the ex- tract and reanalyze.

  - If the measurement of the peak re- sponse is prevented by the presence of inter- ferences, further cleanup is required.

  - Calculations

  - Determine the concentration of indi- vidual compounds in the sample.

    - If the external standard calibration procedure is used, calculate the amount of material injected from the peak response using the calibration curve or calibration factor determined in Section 7.2.2. The con- centration in the sample can be calculated from Equation 2.

AVt 

## Concentration (g/L) 

Vi Vs 

A = Amount of material injected (ng). Vi = Volume of extract injected (L). Vt = Volume of total extract (L).

Vs = Volume of water extracted (mL).

    - If the internal standard calibration procedure is used, calculate the concentra- tion in the sample using the response factor (RF) determined in Section 7.3.2 and Equa- tion 3.

As Is 

## Concentration (g/L) 

Ais RFVo 

Equation   3

where:

As  = Response for the parameter to be meas- ured.

Ais = Response for the internal standard.

Is   =  Amount  of  internal  standard  added  to each extract (g).

Vo = Volume of water extracted (L).

  - When it is apparent that two or more PCB (Aroclor) mixtures are present, the Webb and McCall procedure 16 may be used to identify and quantify the Aroclors.

  - For	multicomponent	mixtures (chlordane, toxaphene, and PCBs) match re- tention times of peaks in the standards with peaks in the sample. Quantitate every iden- tifiable peak unless interference with indi- vidual peaks persist after cleanup. Add peak height or peak area of each identified peak in the chromatogram. Calculate as total re- sponse in the sample versus total response in the standard.

  - Report results in g/L without correc-

tion  for  recovery  data.  All  QC  data  obtained should be reported with the sample results.

  - Method Performance

  - The method detection limit (MDL) is defined as the minimum concentration of a substance that can be measured and reported with 99% confidence that the value is above zero. 1 The MDL concentrations listed  in Table 1 were obtained using reagent water. 17 Similar results were achieved using rep- resentative wastewaters. The MDL actually achieved in a given analysis will vary de- pending on instrument sensitivity and ma- trix  effects.

  - This method has been tested for lin- earity of spike recovery from reagent water and has been demonstrated to be applicable over the concentration  range  from  4  MDL to 1000 MDL with the following exceptions: Chlordane recovery at 4 MDL was  low (60%); Toxaphene recovery was demonstrated linear over the range of 10 MDL to 1000  MDL.  17

  - This method was tested by 20 labora- tories  using  reagent  water,  drinking  water,

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 608

surface water, and three industrial wastewaters spiked at six concentrations. 18 Concentrations used in the  study  ranged from 0.5 to 30 g/L for single-component pes- ticides and from 8.5 to 400 g/L for multi- component parameters. Single operator pre- cision, overall precision, and method accu- racy were found to be directly related to the concentration of the parameter and essen- tially independent of the sample matrix. Linear equations to describe these relation- ships are presented in Table 4.

REFERENCES

    - 40 CFR part 136, appendix B.

    - ‘‘Determination  of  Pesticides   and   PCBs in  Industrial  and  Municipal   Wastewaters,’’ EPA 600/4–82–023, National Technical Infor- mation Service, PB82–214222, Springfield, Virginia 22161, April 1982.

    - ASTM Annual Book of Standards, Part 31, D3694–78. ‘‘Standard Practices for Prepa- ration of Sample Containers and for Preser- vation of Organic Constituents,’’ American Society for Testing and Materials, Philadel- phia.

    - Giam, C.S., Chan, H.S., and Nef, G.S., ‘‘Sensitive Method for Determination of Phthalate Ester Plasticizers in Open-Ocean Biota Samples,’’ Analytical Chemistry, 47, 2225 (1975).

    - Giam, C.S., Chan,  H.S.  ‘‘Control  of Blanks in the Analysis of Phthalates in Air and Ocean Biota Samples,’’ U.S. National Bureau of Standards,  Special  Publication 442, pp. 701–708, 1976.

    - ‘‘Carcinogens—Working With Carcino- gens,’’ Department of Health, Education, and Welfare, Public Health Service, Center for Disease Control, National Institute for Occu- pational Safety and Health, Publication No. 77–206, August 1977.

    - ‘‘OSHA Safety and Health Standards, General Industry,’’ (29 CFR part 1910), Occu- pational Safety and Health Administration, OSHA 2206 (Revised, January 1976).

    - ‘‘Safety in Academic Chemistry Labora- tories,’’ American Chemical Society Publica- tion, Committee on Chemical Safety, 3rd Edition, 1979.

    - Mills, P.A. ‘‘Variation of Florisil Activ- ity: Simple Method for Measuring Absorbent

Capacity and Its Use  in  Standardizing Florisil Columns,’’ Journal  of  the  Association of Official Analytical Chemists, 51, 29, (1968).

    - Provost,   L.P.,  and   Elder,   R.S.  ‘‘Inter- pretation  of  Percent  Recovery  Data,’’  Amer- ican Laboratory, 15, 58–63 (1983). (The value

2.44 used in the equation in Section 8.3.3 is two times the value 1.22 derived in this re- port.)

    - ASTM Annual Book of Standards, Part 31, D3370–76. ‘‘Standard Practices for Sam- pling Water,’’ American Society for Testing and  Materials,  Philadelphia.

    - ‘‘Methods 330.4 (Titrimetric, DPD-FAS) and 330.5 (Spectrophotometric, DPD) for Chlorine, Total Residual,’’ Methods for Chemical Analysis of Water and Wastes, EPA–600/4–79–020, U.S. Environmental Pro- tection Agency, Environmental Monitoring and Support Laboratory, Cincinnati, Ohio 45268, March 1979.

    - Goerlitz,  D.F.,  and  Law,  L.M.   Bulletin for Environmental Contamination and  Toxi- cology, 6, 9 (1971).

    - ‘‘Manual of Analytical Methods for the Analysis of Pesticides in Human and Envi- ronmental Samples,’’ EPA–600/8–80–038, U.S. Environmental Protection Agency, Health Effects Research Laboratory, Research Tri- angle  Park,  North  Carolina.

    - Burke, J.A. ‘‘Gas Chromatography for Pesticide Residue Analysis; Some Practical Aspects,’’ Journal of the Association of Official Analytical Chemists, 48, 1037 (1965).

    - Webb,   R.G.,   and   McCall,   A.C.   ‘‘Quan- titative  PCB  Standards  for  Election  Capture Gas	Chromatography,’’	Journal	of Chromatographic Science, 11, 366 (1973).

    - ‘‘Method Detection Limit  and  Analyt- ical Curve Studies, EPA Methods 606, 607, and 608,’’ Special letter report for EPA Con- tract 68–03–2606, U.S. Environmental Protec- tion Agency, Environmental Monitoring and Support Laboratory, Cincinnati, Ohio 45268, June 1980.

    - ‘‘EPA Method Study 18 Method 608— Organochlorine Pesticides and PCBs,’’ EPA 600/4–84–061, National Technical Information Service, PB84–211358, Springfield, Virginia 22161, June 1984.

TABLE 1—CHROMATOGRAPHIC CONDITIONS AND METHOD DETECTION LIMITS

| Parameter | Retention time (min) | Method detec- tion limit (g/L) |
| --- | --- | --- |
|  | Col. 1 | Col. 2 |  |
| a-BHC ....................................................................................................................... | 1.35 | 1.82 | 0.003 |
| g-BHC ........................................................................................................................ | 1.70 | 2.13 | 0.004 |
| b-BHC ........................................................................................................................ | 1.90 | 1.97 | 0.006 |
| Heptachlor ................................................................................................................. | 2.00 | 3.35 | 0.003 |
| d-BHC ........................................................................................................................ | 2.15 | 2.20 | 0.009 |
| Aldrin ......................................................................................................................... | 2.40 | 4.10 | 0.004 |
| Heptachlor epoxide ................................................................................................... | 3.50 | 5.00 | 0.083 |
| Endosulfan I .............................................................................................................. | 4.50 | 6.20 | 0.014 |
| 4,4-DDE .................................................................................................................... | 5.13 | 7.15 | 0.004 |
| Dieldrin ...................................................................................................................... | 5.45 | 7.23 | 0.002 |

#### Pt. 136, App. A, Meth. 608

40 CFR Ch. I (7–1–17 Edition)

TABLE 1—CHROMATOGRAPHIC CONDITIONS AND METHOD DETECTION LIMITS—Continued

| Parameter | Retention time (min) | Method detec- tion limit (g/L) |
| --- | --- | --- |
|  | Col. 1 | Col. 2 |  |
| Endrin ........................................................................................................................ 4,4-DDD .................................................................................................................... Endosulfan II ............................................................................................................. 4,4-DDT .................................................................................................................... Endrin aldehyde ........................................................................................................ Endosulfan sulfate ..................................................................................................... Chlordane .................................................................................................................. Toxaphene ................................................................................................................. PCB–1016 ................................................................................................................. PCB–1221 ................................................................................................................. PCB–1232 ................................................................................................................. PCB–1242 ................................................................................................................. PCB–1248 ................................................................................................................. PCB–1254 ................................................................................................................. PCB–1260 ................................................................................................................. | 6.55 7.83 8.00 9.40 11.82 14.22 mr mr mr mr mt mr mr mr mr | 8.10 9.08 8.28 11.75 9.30 10.70 mr mr mr mr mr mr mr mr mr | 0.006 0.011 0.004 0.012 0.023 0.066 0.014 0.24 nd nd nd 0.065 nd nd nd |

Column 1 conditions: Supelcoport (100/120 mesh) coated with 1.5% SP–2250/1.95% SP–2401 packed in a 1.8 m long 4 mm ID glass column with 5% methane/95% argon carrier gas at 60 mL/min flow rate. Column temperature held isothermal at 200 C, except for PCB–1016 through PCB–1248, should be measured at 160 C.

Column 2 conditions: Supelcoport (100/120 mesh) coated with 3% OV–1 packed in a 1.8 m long 4 mm ID glass column with 5% methane/95% argon carrier gas at 60 mL/min flow rate. Column temperature held isothermal at 200 C for the pesticides; at 140 C for PCB–1221 and 1232; and at 170 C for PCB–1016 and 1242 to 1268.

mr = Multiple peak response. See Figures 2 thru 10. nd = Not determined.

TABLE 2—DISTRIBUTION OF CHLORINATED PESTICIDES AND PCBS INTO FLORISIL COLUMN FRACTIONS  2

| Parameter | Percent recovery by fraction a |
| --- | --- |
|  | 1 | 2 | 3 |
| Aldrin ............................................................................................................................. | 100 | 100 | 91 |
| a-BHC ........................................................................................................................... | 100 |  |  |
| b-BHC ............................................................................................................................ | 97 |  |  |
| d-BHC ............................................................................................................................ | 98 |  |  |
| g-BHC ............................................................................................................................ | 100 |  |  |
| Chlordane ...................................................................................................................... | 100 |  |  |
| 4,4–DDD ....................................................................................................................... | 99 |  |  |
| 4,4–DDE ....................................................................................................................... | 98 |  |  |
| 4,4–DDT ....................................................................................................................... | 100 |  |  |
| Dieldrin .......................................................................................................................... | 0 |  |  |
| Endosulfan I .................................................................................................................. | 37 | 64 |  |
| Endosulfan II ................................................................................................................. | 0 | 7 |  |
| Endosulfan sulfate ......................................................................................................... | 0 | 0 | 106 |
| Endrin ............................................................................................................................ | 4 | 96 |  |
| Endrin aldehyde ............................................................................................................ | 0 | 68 | 26 |
| Heptachlor ..................................................................................................................... | 100 |  |  |
| Heptachlor epoxide ....................................................................................................... | 100 |  |  |
| Toxaphene ..................................................................................................................... | 96 |  |  |
| PCB–1016 ..................................................................................................................... | 97 |  |  |
| PCB–1221 ..................................................................................................................... | 97 |  |  |
| PCB–1232 ..................................................................................................................... | 95 | 4 |  |
| PCB–1242 ..................................................................................................................... | 97 |  |  |
| PCB–1248 ..................................................................................................................... | 103 |  |  |
| PCB–1254 ..................................................................................................................... | 90 |  |  |
| PCB–1260 ..................................................................................................................... | 95 |  |  |

a Eluant composition:

Fraction 1–6% ethyl ether in hexane. Fraction 2–15% ethyl ether in hexane. Fraction 3–50% ethyl ether in hexane.

TABLE 3—QC ACCEPTANCE CRITERIA—METHOD 608

| Parameter | Test conc. (g/L) | Limit for s (g/L) | Range for X¯ (g/L) | Range for P, Ps(%) |
| --- | --- | --- | --- | --- |
| Aldrin ..................................................................................................... | 2.0 | 0.42 | 1.08–2.24 | 42–122 |
| a-BHC ................................................................................................... | 2.0 | 0.48 | 0.98–2.44 | 37–134 |
| b-BHC .................................................................................................... | 2.0 | 0.64 | 0.78–2.60 | 17–147 |
| d-BHC .................................................................................................... | 2.0 | 0.72 | 1.01–2.37 | 19–140 |

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 608

TABLE 3—QC ACCEPTANCE CRITERIA—METHOD 608—Continued

| Parameter | Test conc. (g/L) | Limit for s (g/L) | Range for X¯ (g/L) | Range for P, Ps(%) |
| --- | --- | --- | --- | --- |
| g-BHC .................................................................................................... | 2.0 | 0.46 | 0.86–2.32 | 32–127 |
| Chlordane .............................................................................................. | 50 | 10.0 | 27.6–54.3 | 45–119 |
| 4,4–DDD .............................................................................................. | 10 | 2.8 | 4.8–12.6 | 31–141 |
| 4,4–DDE .............................................................................................. | 2.0 | 0.55 | 1.08–2.60 | 30–145 |
| 4,4–DDT ............................................................................................... | 10 | 3.6 | 4.6–13.7 | 25–160 |
| Dieldrin .................................................................................................. | 2.0 | 0.76 | 1.15–2.49 | 36–146 |
| Endosulfan I .......................................................................................... | 2.0 | 0.49 | 1.14–2.82 | 45–153 |
| Endosulfan II ......................................................................................... | 10 | 6.1 | 2.2–17.1 | D–202 |
| Endosulfan Sulfate ................................................................................ | 10 | 2.7 | 3.8–13.2 | 26–144 |
| Endrin .................................................................................................... | 10 | 3.7 | 5.1–12.6 | 30–147 |
| Heptachlor ............................................................................................. | 2.0 | 0.40 | 0.86–2.00 | 34–111 |
| Heptachlor epoxide ............................................................................... | 2.0 | 0.41 | 1.13–2.63 | 37–142 |
| Toxaphene ............................................................................................ | 50.0 | 12.7 | 27.8–55.6 | 41–126 |
| PCB-1016 .............................................................................................. | 50 | 10.0 | 30.5–51.5 | 50–114 |
| PCB-1221 .............................................................................................. | 50 | 24.4 | 22.1–75.2 | 15–178 |
| PCB-1232 .............................................................................................. | 50 | 17.9 | 14.0–98.5 | 10–215 |
| PCB-1242 .............................................................................................. | 50 | 12.2 | 24.8–69.6 | 39–150 |
| PCB-1248 .............................................................................................. | 50 | 15.9 | 29.0–70.2 | 38–158 |
| PCB-1254 .............................................................................................. | 50 | 13.8 | 22.2–57.9 | 29–131 |
| PCB-1260 .............................................................................................. | 50 | 10.4 | 18.7–54.9 | 8–127 |

s = Standard deviation of four recovery measurements, in g/L (Section 8.2.4). X¯ = Average recovery for four recovery measurements, in g/L (Section 8.2.4).

P, Ps  = Percent recovery measured (Section 8.3.2, Section 8.4.2). D = Detected; result must be greater than zero.

NOTE: These criteria are based directly upon the method performance data in Table 4. Where necessary, the limits for recov- ery have been broadened to assure applicability of the limits to concentrations below those used to develop Table 4.

TABLE 4—METHOD ACCURACY AND PRECISION AS FUNCTIONS OF CONCENTRATION—METHOD 608

| Parameter | Accuracy, as recov- ery, X(g/L) | Single analyst pre- cision, sr(g/L) | Overall precision, S(g/L) |
| --- | --- | --- | --- |
| Aldrin ......................................................................................... | 0.81C + 0.04 | 0.16X¯ ¥0.04 | 0.20X¯ ¥0.01 |
| a-BHC ....................................................................................... | 0.84C + 0.03 | 0.13X¯ + 0.04 | 0.23X¯ ¥0.00 |
| b-BHC ........................................................................................ | 0.81C + 0.07 | 0.22X¯ ¥0.02 | 0.33X¥0.05 |
| d-BHC ........................................................................................ | 0.81C + 0.07 | 0.18X¯ + 0.09 | 0.25X¯ + 0.03 |
| g-BHC ........................................................................................ | 0.82C¥0.05 | 0.12X¯ + 0.06 | 0.22X¯ + 0.04 |
| Chlordane .................................................................................. | 0.82C¥0.04 | 0.13X¯ + 0.13 | 0.18X¯ + 0.18 |
| 4,4-DDD .................................................................................... | 0.84C + 0.30 | 0.20X¯ ¥0.18 | 0.27X¯ ¥0.14 |
| 4,4-DDE .................................................................................... | 0.85C + 0.14 | 0.13X¯ + 0.06 | 0.28X¯ ¥0.09 |
| 4,4-DDT .................................................................................... | 0.93C¥0.13 | 0.17X¯ + 0.39 | 0.31X¯ ¥0.21 |
| Dieldrin ...................................................................................... | 0.90C + 0.02 | 0.12X¯ + 0.19 | 0.16X¯ + 0.16 |
| Endosulfan I .............................................................................. | 0.97C + 0.04 | 0.10X¯ + 0.07 | 0.18X¯ + 0.08 |
| Endosulfan II ............................................................................. | 0.93C + 0.34 | 0.41X¯ —0.65 | 0.47X¯ ¥0.20 |
| Endosulfan Sulfate .................................................................... | 0.89C¥0.37 | 0.13X¯ + 0.33 | 0.24X¯ + 0.35 |
| Endrin ........................................................................................ | 0.89C¥0.04 | 0.20X¯ + 0.25 | 0.24X¯ + 0.25 |
| Heptachlor ................................................................................. | 0.69C + 0.04 | 0.06X¯ + 0.13 | 0.16X¯ + 0.08 |
| Heptachlor epoxide ................................................................... | 0.89C + 0.10 | 0.18X¯ ¥0.11 | 0.25X¯ ¥0.08 |
| Toxaphene ................................................................................. | 0.80C + 1.74 | 0.09X¯ + 3.20 | 0.20X¯ + 0.22 |
| PCB–1016 ................................................................................. | 0.81C + 0.50 | 0.13X¯ + 0.15 | 0.15X¯ + 0.45 |
| PCB–1221 ................................................................................. | 0.96C + 0.65 | 0.29X¯ ¥0.76 | 0.35X¯ ¥0.62 |
| PCB–1232 ................................................................................. | 0.91C + 10.79 | 0.21X¯ ¥1.93 | 0.31X¯ + 3.50 |
| PCB–1242 ................................................................................. | 0.93C + 0.70 | 0.11X¯ + 1.40 | 0.21X¯ + 1.52 |
| PCB–1248 ................................................................................. | 0.97C + 1.06 | 0.17X¯ + 0.41 | 0.25X¯ ¥0.37 |
| PCB–1254 ................................................................................. | 0.76C + 2.07 | 0.15X¯ + 1.66 | 0.17X¯ + 3.62 |
| PCB–1260 ................................................................................. | 0.66C + 3.76 | 0.22X¯ ¥2.37 | 0.39X¯ ¥4.86 |

X= Expected recovery for one or more measurements of a sample containing a concentration of C, in g/L.

sr= Expected single analyst standard deviation of measurements at an average concentration found of X¯ , in g/L. S= Expected interlaboratory standard deviation of measurements at an average concentration found of X¯ , in g/L. C = True value for the concentration, in g/L.

X¯ = Average recovery found for measurements of samples containing a concentration of C, in g/L.

#### Pt. 136, App. A, Meth. 608

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 608

Pt. 136, App. A, Meth. 608

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 608

Pt. 136, App. A, Meth. 608

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 608

Pt. 136, App. A, Meth. 608

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 608

Pt. 136, App. A, Meth. 608

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 609

METHOD 609—NITROAROMATICS AND

ISOPHORONE

- Scope and Application

  - This method covers the determination of certain nitroaromatics and isophorone. The following parameters may be deter- mined by this method:

| Parameter | STORET No. | CAS No. |
| --- | --- | --- |
| 2,4-Dinitrotoluene ...................... | 34611 | 121–14–2 |
| 2,6-Dinitrotoluene ...................... | 34626 | 606–20–2 |
| Isophorone ................................. | 34408 | 78–59–1 |
| Nitrobenzene ............................. | 34447 | 98–95–3 |

  - This  is  a  gas  chromatographic  (GC) method  applicable  to  the  determination  of

#### Pt. 136, App. A, Meth. 609

the compounds listed above in municipal and industrial discharges as  provided  under  40 CFR 136.1. When this method is used to  ana- lyze unfamiliar samples for any or all of the compounds above, compound identifications should be supported by  at  least  one  addi- tional qualitative technique. This method describes  analytical  conditions  for  a  second gas  chromatographic  column  that   can   be used  to  confirm  measurements  made  with the primary column. Method 625 provides gas chromatograph/mass spectrometer (GC/MS) conditions  appropriate  for   the   qualitative and  quantitative  confirmation  of  results   for all of the parameters listed above, using the extract  produced  by  this  method.

  - The method detection limit (MDL, de- fined in Section 14.1) 1 for each parameter is listed in Table 1. The MDL for a specific wastewater may differ from those listed, de- pending upon the nature of interferences  in the sample matrix.

  - The sample extraction and concentra- tion steps in this method are essentially the same as in Methods 606, 608, 611, and 612. Thus, a single sample may be extracted to measure the parameters included in the scope of each of these methods. When clean- up is required, the concentration levels must be high enough to permit selecting aliquots, as necessary, to apply appropriate cleanup procedures. The analyst is allowed the lati- tude, under Section 12, to select chromatographic conditions appropriate for the simultaneous measurement of combina- tions of these parameters.

  - Any modification of this method,  be- yond those expressly permitted, shall be con- sidered as a major modification subject to application and approval of alternate test procedures under 40 CFR 136.4 and 136.5.

  - This method is restricted to use by or under the supervision of analysts experi- enced in the use of a gas chromatograph and in the interpretation of gas chromatograms. Each analyst must demonstrate  the  ability to generate acceptable results with this method using the procedure described in Sec- tion 8.2.

- Summary of Method

  - A measured volume of sample, ap- proximately 1–L, is extracted with  meth- ylene chloride using a separatory funnel. The methylene chloride extract is dried and ex- changed to hexane during concentration to a volume of 10 mL or less. Isophorone and nitrobenzene are measured by flame ioniza- tion detector gas chromatography (FIDGC). The dinitrotoluenes are measured by elec- tron capture detector gas chromatography (ECDGC). 2

  - The method provides a Florisil column cleanup procedure to aid  in  the  elimination of interferences that may be encountered.

#### 40 CFR Ch. I (7–1–17 Edition)

- Interferences

  - Method interferences may be caused by contaminants in solvents, reagents, glass- ware, and other sample processing hardware that lead to discrete artifacts and/or ele- vated baseliles in gas chromatograms. All of these materials must be routinely dem- onstrated to be free from interferences under the conditions of the analysis by running laboratory reagent blanks as described in Section 8.1.3.

    - Glassware must be scrupulously cleaned. 3 Clean all glassware as soon as pos- sible after use by rinsing with the last sol- vent used in it. Solvent rinsing should be fol- lowed by detergent washing with hot water, and rinses with tap water and distilled water. The glassware should then be drained dry, and heated in a muffle furnace at 400 C for 15 to 30 min. Some thermally stable ma- terials, such as PCBs, may not be eliminated by this treatment. Solvent rinses with ace- tone and pesticide quality hexane may be substituted for the muffle furnace heating. Thorough rinsing with such solvents usually eliminates PCB interference. Volumetric ware should not be heated in a muffle fur- nace. After drying and cooling, glassware should be sealed and stored in a clean envi- ronment to prevent any accumulation of dust or other contaminants. Store inverted or capped with aluminum foil.

    - The use of high purity reagents and solvents helps to minimize interference prob- lems. Purification of solvents  by  distillation in all-glass systems may be required.

3.2 Matrix interferences may be caused by contaminants that are co-extracted from the sample. The extent of matrix interferences will vary considerably from source to source, depending upon the nature and diversity  of the industrial complex or municipality being sampled.  The  cleanup  procedure  in  Section

11 can be used to overcome many of these interferences, but unique samples may re- quire additional cleanup approaches to achieve the MDL listed in Table 1.

- Safety

4.1   The   toxicity   or   carcinogenicity   of each  reagent  used  in  this  method  has  not been precisely defined; however, each chem- ical compound should be treated as a poten- tial health hazard. From this viewpoint, ex- posure to these chemicals must be reduced to the lowest possible level by whatever means available. The laboratory is responsible for maintaining   a   current   awareness   file   of OSHA  regulations  regarding  the  safe  han- dling of the chemicals specified in this meth- od. A reference file of material data handling sheets should also be made available to all personnel involved in the chemical analysis. Additional  references  to  laboratory  safety are available and have been identified 4M6 for the information of the analyst.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 609

- Apparatus and Materials

  - Sampling equipment, for discrete or composite  sampling.

    - Grab sample bottle—1–L or 1-qt, amber glass, fitted with a screw cap lined with Teflon. Foil may be substituted for Tef- lon if the sample is not corrosive. If amber bottles are not available, protect samples from light. The bottle and cap liner must be washed, rinsed with acetone or methylene chloride, and dried before use to minimize contamination.

    - Automatic sampler (optional)—The sampler must incorporate glass sample con- tainers for the collection of a minimum of 250 mL of sample. Sample containers must be kept refrigerated at 4 C and protected from light during compositing. If the sampler uses a peristaltic pump, a minimum length of compressible silicone rubber tubing may be used. Before use, however, the compressible tubing should be thoroughly rinsed with methanol, followed by repeated rinsings with distilled water to minimize the potential for contamination of the sample. An integrating flow meter is required to collect flow propor- tional  composites.

  - Glassware (All specifications are sug- gested. Catalog numbers are included for il- lustration only.):

    - Separatory funnel—2–L, with Teflon stopcock.

    - Drying column—Chromatographic column, approximately 400 mm long 19 mm ID,  with  coarse  frit  filter  disc.

    - Chromatographic column—100 mm long 10 mm ID, with Teflon stopcock.

    - Concentrator tube, Kuderna-Dan- ish—10-mL, graduated (Kontes K–570050–1025 or equivalent). Calibration must  be  checked at the volumes employed in the test. Ground glass stopper is used to prevent evaporation of  extracts.

    - Evaporative flask, Kuderna-Danish— 500-mL (Kontes K–570001–0500 or equivalent). Attach  to  concentrator  tube  with  springs.

    - Snyder column, Kuderna-Danish— Three-ball macro (Kontes K–503000–0121 or equivalent).

    - Snyder column, Kuderna-Danish— Two-ball micro (Kontes K–569001–0219 or equivalent).

    - Vials—10 to 15-mL, amber glass, with Teflon-lined screw cap.

  - Boiling chips—Approximately 10/40 mesh. Heat to 400 C for 30 min or Soxhlet ex- tract  with  methylene  chloride.

  - Water bath—Heated, with concentric ring cover, capable of temperature control (2 C). The bath should be used in a hood.

  - Balance—Analytical, capable of accu- rately weighing 0.0001 g.

  - Gas chromatograph—An analytical system complete with gas chromatograph suitable for on-column injection and all re- quired  accessories  including  syringes,  ana-

lytical columns, gases, detector, and strip- chart recorder. A data system is rec- ommended for measuring peak areas.

    - Column 1—1.2 m long 2 or 4 mm ID

glass, packed with 1.95% QF–1/1.5% OV–17 on Gas-Chrom Q (80/100 mesh) or equivalent. This column was used to develop the method performance statements given in Section 14. Guidelines for the use of alternate column packings are provided in Section 12.1.

    - Column 2—3.0 m long 2 or 4 mm ID

glass, packed with 3% OV–101 on Gas-Chrom Q (80/100 mesh) or equivalent.

    - Detectors—Flame ionization and electron capture detectors. The flame ioniza- tion detector (FID) is used when determining isophorone and nitrobenzene. The electron capture detector (ECD) is used when deter- mining the dinitrotoluenes. Both detectors have proven effective in the analysis of wastewaters and were used in develop the method  performance  statements  in  Section

- Guidelines for the use to alternate detec- tors are provided in Section 12.1.

  - Reagents

  - Reagent water—Reagent water is de- fined as a water in which an  interferent  is not observed at the  MDL  of  the  parameters of  interest.

  - Sodium hydroxide solution (10 N)— Dissolve 40 g of NaOH (ACS) in reagent water and dilute to 100 mL.

  - Sulfuric acid (1 + 1)—Slowly, add  50 mL of  H2SO4 (ACS, sp.  gr.  1.84) to  50  mL of reagent water.

  - Acetone, hexane, methanol, methylene chloride—Pesticide quality or equivalent.

  - Sodium sulfate—(ACS) Granular, an- hydrous. Purify by heating at 400 C for 4 h in a shallow tray.

  - Florisil—PR grade (60/100 mesh). Pur- chase activated at 1250  F and store in dark in glass containers with ground glass stop- pers or foil-lined screw caps. Before use, acti- vate each batch at least 16 h at 200 C in a foil-covered glass container and  allow  to cool.

  - Stock standard solutions (1.00 g/L)—

Stock standard solutions can be prepared from pure standard materials or purchased as certified solutions.

    - Prepare stock standard solutions by accurately weighing about 0.0100 g of pure material.  Dissolve   the   material   in   hexane and dilute to volume in a 10-mL volumetric flask. Larger volumes can be used at the con- venience of the analyst. When compound pu- rity is assayed to be  96%  or  greater,  the weight can be used without correction to cal- culate the concentration of the stock stand- ard. Commercially  prepared  stock  standards can be used at any concentration if they are certified by the manufacturer or by an inde- pendent  source.

    - Transfer the stock standard solu- tions   into   Teflon-sealed   screw-cap   bottles.

#### Pt. 136, App. A, Meth. 609

Store at 4 C and protect from light. Stock standard solutions should be checked fre- quently for signs of degradation or evapo- ration, especially just prior to preparing calibration standards from them.

    - Stock standard solutions must be re- placed after six months, or sooner if com- parison with check standards indicates a problem.

6.8 Quality control check sample con- centrate—See Section 8.2.1.

  - Calibration

  - Establish gas chromatographic oper- ating conditions equivalent to those given in Table 1. The gas chromatographic system can be calibrated using the external standard technique (Section 7.2) or the internal stand- ard technique (Section 7.3).

  - External standard calibration proce- dure:

    - Prepare calibration standards at a minimum of three concentration levels  for each parameter of interest by adding vol- umes of one or more stock standards to a volumetric flask and diluting to volume with hexane. One of the external standards should be at a concentration near, but above, the MDL (Table 1) and the other concentrations should correspond to the expected range of concentrations found in real samples or should define the working range of the detec- tor.

    - Using injections of 2 to 5 L, analyze

each calibration standard according to Sec- tion 12 and tabulate peak height or area re- sponses against  the mass injected. The re- sults can be used to prepare a calibration curve for each compound. Alternatively, if the ratio of response to amount injected (calibration factor) is a constant over the working range (<10% relative standard devi- ation, RSD) linearity through the origin can be assumed and the average ratio or calibra- tion factor can be used in place of a calibra- tion curve.

  - Internal standard calibration proce- dure—To use this approach, the analyst must select one or more internal standards that are similar in analytical behavior to the compounds of interest. The analyst must fur- ther demonstrate that the measurement of the internal standard is not affected by method or matrix interferences. Because of these limitations, no internal standard  can be suggested that is applicable to all sam- ples.

    - Prepare calibration standards at a minimum of three concentration levels  for each parameter of interest by adding vol- umes of one or more stock standards to a volumetric flash. To each calibration stand- ard, add a known constant amount of one or more internal standards, and dilute to vol- ume with hexane. One of the standards should be at a concentration near, but above, the   MDL   and   the   other   concentrations

#### 40 CFR Ch. I (7–1–17 Edition)

should correspond to the expected range of concentrations found in real samples or should define the working range of the detec- tor.

    - Using injections of 2 to 5 L, analyze

each calibration standard according to Sec- tion 12 and tabulate peak height or area re- sponses against concentration for each com- pound and internal standard. Calculate re- sponse factors (RF) for each compound using Equation 1.

Equation 1.

As Cis 

## RF 

Ais Cs 

where:

As  = Response for the parameter to be meas- ured.

Ais = Response for the internal standard.

Cis  = Concentration of the internal standard (g/L).

Cs   =  Concentration  of  the  parameter  to  be measured (g/L).

If the RF value over the working range is a constant (<10% RSD), the RF can be as- sumed to be invariant and the average RF can be used for calculations. Alternatively, the results can be used to plot a calibration curve of response ratios, As/Ais, vs. RF.

  - The working calibration curve, cali- bration factor, or RF must be verified on each working day by the measurement of one or more calibration standards. If the re- sponse for any parameter varies from the predicted response by more than 15%, a new calibration curve must be prepared for that compound.

  - Before using any cleanup procedure, the analyst must process a series of calibra- tion standards through the procedure to vali- date elution patterns and the absence of interferences from the reagents.

  - Quality Control

  - Each laboratory that uses this method is required to operate a formal quality  con- trol program. The minimum requirements of this program consist of an initial demonstra- tion of laboratory capability and an ongoing analysis of spiked samples to evaluate and document data quality. The laboratory must maintain records to document the quality of data that is generated. Ongoing data quality checks are compared with established per- formance criteria to determine if the results of analyses meet the performance character- istics of the method. When results of sample spikes indicate atypical method perform- ance, a quality control check  standard  must be analyzed to confirm that the measure- ments were performed in an in-control mode of operation.

    - The analyst must make an initial, one-time,  demonstration  of  the  ability  to

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 609

generate acceptable accuracy and precision with this method. This ability is established as described in Section 8.2.

    - In recognition of advances that are occurring in chromatography, the analyst is permitted certain options (detailed in Sec- tions 10.4, 11.1, and 12.1) to improve the sepa- rations or lower the cost of measurements. Each time such a modification is  made  to the method, the analyst is required to repeat the procedure in Section 8.2.

    - Before processing any samples, the analyst must analyze a  reagent  water  blank to demonstrate that interferences from the analytical system and glassware are under control. Each time a set of samples is ex- tracted or reagents are changed, a reagent water blank must be processed as a safe- guard  against  laboratory  contamination.

    - The laboratory must, on an ongoing basis, spike and analyze a minimum of 10% of all samples to monitor and evaluate lab- oratory data quality. This procedure is de- scribed in Section 8.3.

8.1,5 The laboratory must, on an ongoing basis, demonstrate through the analyses of quality control  check standards  that  the op- eration of the measurement system is in con- trol.  This  procedure  is  described  in  Section

8.4. The frequency of the check standard analyses is equivalent to 10% of all samples analyzed but may be reduced if spike recov- eries from samples (Section 8.3) meet all specified quality control criteria.

8.1.6 The laboratory must maintain per- formance records to document the quality of data that is generated. This procedure is de- scribed in Section 8.5.

  - To establish the ability to generate acceptable accuracy and precision, the ana- lyst must perform the following operations.

    - A quality control (QC) check sample concentrate is required containing each pa- rameter of interest in acetone at a con- centration of 20 g/mL for each dinitro- toluene and 100 g/mL for isophorone and nitrobenzene. The QC check sample con- centrate must be obtained from the U.S. En- vironmental Protection Agency, Environ- mental Monitoring and Support  Laboratory in Cincinnati, Ohio, if available. If not avail- able from that source, the QC check sample concentrate must be obtained from another external source. If not available from either source above, the QC check sample con- centrate must be prepared by the laboratory using stock standards prepared independ- ently from those used for calibration.

    - Using a pipet, prepare QC check sam- ples at the test concentrations  shown  in Table 2 by adding 1.00 mL  of  QC  check  sam- ple concentrate to each  of  four  1–L  aliquots of  reagent  water.

    - Analyze the well-mixed QC check samples according to the  method  beginning in Section 10.

    - Calculate the average recovery (X¯ ) in

g/L, and the standard deviation of the re- covery (s) in g/L, for each parameter using the four results.

    - For each parameter compare s and X¯

with the corresponding acceptance criteria for   precision   and   accuracy,   respectively,

found in Table 2. If s and X¯  for all param-

eters of interest meet the acceptance cri- teria, the system performance is acceptable and analysis of actual samples can begin. If any individual s exceeds the precision limit

or any individual X¯  falls outside the range

for accuracy, the system performance is un- acceptable for that parameter. Locate and correct the source of the problem and repeat the test for all parameters of interest begin- ning with Section 8.2.2.

  - The laboratory must, on an ongoing basis, spike at least 10% of the samples from each sample site being monitored to assess accuracy. For laboratories analyzing one to ten samples per month, at least one spiked sample per month is required.

    - The concentration of the spike in the sample should be determined as follows:

      - If, as in compliance monitoring, the concentration of a specific parameter in the sample is being checked against a regu- latory concentration limit, the spike should be at that limit or 1 to 5 times higher than the background concentration determined in Section 8.3.2, whichever concentration would be larger.

      - If the concentration of a specific parameter in the sample  is  not  being checked against a limit specific to that pa- rameter, the spike should be at the test con- centration in Section 8.2.2 or 1 to 5 times higher than the background concentration determined in Section 8.3.2, whichever con- centration would be larger.

      - If it is impractical to determile background levels before spiking (e.g., max- imum holding times will be exceeded), the spike concentration should be (1) the regu- latory concentration limit, if any; or, if none

(2) the larger of either 5  times  higher  than the expected  background  concentration  or the test concentration in Section 8.2.2.

    - Analyze one sample aliquot to deter- mine the background concentration (B) of each parameter. If necessary, prepare a new QC check sample concentrate (Section 8.2.1) appropriate for the background concentra- tions in the sample. Spike a second sample aliquot with 1.0 mL of the QC check sample concentrate and analyze it to determine the concentration after spiking (A) of each pa- rameter. Calculate each percent recovery (P) as 100 (A¥B)%/T, where T is the known true value of the spike.

    - Compare the percent recovery (P) for each parameter with the corresponding QC acceptance criteria found in Table 2. These acceptance criteria were calculated to in- clude an allowance for error in measurement

#### Pt. 136, App. A, Meth. 609

of both the background and spike concentra- tions, assuming a spike  to  background  ratio of 5:1. This error will be accounted for to the extent that the analyst’s spike to back- ground ratio approaches 5:1. 7 If spiking was performed at a concentration lower than the test concentration in Section 8.2.2, the ana- lyst must use either the QC acceptance cri- teria in Table 2, or optional QC acceptance criteria calculated for the specific spike con- centration. To calculate optional acceptance criteria for the recovery of a parameter: (1) Calculate accuracy (X) using the equation in Table 3, substituting the spike concentration

(T) for C; (2) calculate overall precision (S) using the equation in Table 3, substituting X for X¯ 8; (3) calculate the range for recovery at

the spike concentration  as  (100  X/T)  2.44 (100 S/T)%. 7

    - If any individual P falls outside the designated range for recovery, that param- eter has failed the acceptance criteria. A check standard containing each parameter that failed the criteria must be analyzed as described in Section 8.4.

  - If any parameter fails the acceptance criteria for recovery in Section 8.3, a QC check standard containing each parameter that failed must be prepared and analyzed.

NOTE: The frequency for the required anal- ysis of a QC check standard will depend upon the number of parameters being simulta- neously tested, the complexity of the sample matrix, and the performance of the labora- tory.

    - Prepare the QC check standard by adding 1.0 mL of QC check sample con- centrate (Section 8.2.1 or 8.3.2) to 1 L of rea- gent water. The QC check standard needs only to contain the parameters that failed criteria in the test in Section 8.3.

    - Analyze the QC check standard to determine the concentration measured (A) of each parameter. Calculate each percent re- covery (Ps) as 100 (A/T)%, where T is the true value of the standard concentration.

    - Compare the percent recovery (Ps) for each parameter with the corresponding QC acceptance criteria found in Table 2. Only parameters that failed the test in Section 8.3 need to be compared with these  criteria.  If the recovery of any such parameter falls out- side the designated range, the laboratory performance for that parameter is judged to be out of control, and the problem must be immediately identified and corrected. The analytical result for that parameter in the unspiked sample is suspect  and may not  be reported for regulatory compliance purposes.

  - As part of QC program for the labora- tory, method accuracy for wastewater sam- ples must be assessed and records must be maintained. After the analysis of five spiked

wastewater samples as in Section 8.3, cal- culate the average percent recovery (P¯ ) and

the standard deviation of the percent recov- ery (sp). Express the accuracy assessment as

#### 40 CFR Ch. I (7–1–17 Edition)

a percent recovery interval from P¯ ¥2sp to P¯

+ 2sp. If P¯  = 90% and sp  = 10%, for example,

the accuracy interval is expressed as 70– 110%. Update the accuracy  assessment  for each parameter on a regular basis (e.g. after each five to  ten  new  accuracy  measure- ments).

  - It is recommended that the laboratory adopt additional quality assurance practices for use  with  this method.  The  specific  prac- tices that  are  most  productive  depend  upon the needs of the laboratory and the nature of the samples. Field duplicates may be ana- lyzed to assess the precision of the environ- mental measurements. When doubt exists over the identification of a peak on the chro- matogram, confirmatory techniques such as gas chromatography with a dissimilar col- umn, specific element detector, or mass spectrometer must be used. Whenever pos- sible, the laboratory should analyze standard reference materials and participate in rel- evant performance evaluation studies.

  - Sample Collection, Preservation, and Handling

  - Grab samples must be collected  in glass containers. Conventional sampling practices 8 should be followed, except  that the bottle must not be prerinsed with sample before collection. Composite samples should be collected in refrigerated  glass  containers in accordance with the requirements of the program. Automatic sampling equipment must be as free as possible of Tygon tubing and other potential sources of contamina- tion.

  - All samples must be iced or refrig- erated at 4 C from the time of collection until   extraction.

  - All samples must be extracted within 7 days of collection and completely analyzed within 40 days of extraction. 2

  - Sample Extraction

  - Mark the water meniscus on the side of the sample bottle  for  later  determination of sample volume. Pour the entire sample into a 2–L separatory  funnel.  Check  the  pH of the sample with wide-range pH paper and adjust to within the range of 5 to 9 with so- dium hydroxide solution or sulfuric acid.

  - Add 60 mL of methylene chloride  to the sample bottle, seal, and shake 30 s to rinse the inner surface. Transfer the solvent to the separatory funnel and extract the sample by shaking the funnel for 2 min. with periodic venting to release excess pressure. Allow the organic layer to separate from the water phase for a minimum of 10 min. If the emulsion interface between layers is more than one-third the volume of  the  solvent layer, the analyst must employ mechanical techniques to complete the phase separation. The optimum technique depends upon the sample,  but  may  include  stirring,  filtration

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 609

of the emulsion through glass wool, cen- trifugation, or other physical methods. Col- lect the methylene chloride extract in a 250- mL Erlenmeyer flask.

  - Add a second 60-mL volume of meth- ylene chloride to the sample bottle and re- peat the extraction procedure a second time, combining the extracts in the Erlenmeyer flask. Perform a third extraction in the same manner.

  - Assemble a Kuderna-Danish (K-D) concentrator by attaching a 10-mL concen- trator tube to a 500-mL evaporative flask. Other concentration devices or  techniques may be used in place of the K-D concentrator if the requirements of Section 8.2 are met.

  - Pour the combined extract through a solvent-rinsed drying column containing about 10 cm of anhydrous sodium sulfate, and collect the extract in the K-D concen- trator. Rinse the Erlenmeyer flask and col- umn with 20 to 30 mL of methylene chloride to complete the quantitative transfer.

  - Sections 10.7 and 10.8 describe a pro- cedure for exchanging the methylene chlo- ride solvent to hexane while concentrating the extract volume to 1.0 mL. When it is not necessary to achieve the MDL in Table 2, the solvent exchange may be made by the addi- tion of 50 mL of hexane and concentration to

10  mL  as  described  in  Method  606,  Sections

10.7 and 10.8.

  - Add one or two clean boiling chips to the evaporative flask and attach a three-ball Snyder column. Prewet the Snyder  column by adding about 1 mL of methylene chloride to the top. Place the K-D apparatus on a hot water bath (60 to 65 C) so that the concen- trator tube is partially immersed in the hot water, and the entire lower rounded surface of the flask is bathed with hot vapor. Adjust the vertical position of the apparatus  and the water temperature as required to com- plete the concentration in 15 to  20  min.  At the proper rate of distillation the balls of the column will actively chatter but the cham- bers will not flood with condensed solvent. When the apparent volume of liquid reaches 1 mL, remove the K-D apparatus and allow it to drain and cool for at least 10 min.

  - Remove the Snyder column and rinse the flask and its lower joint into the concen- trator tube with 1 to 2 mL of methylene chloride. A 5-mL syringe is recommended for this operation.  Add  1  to  2  mL  of  hexane  and a clean boiling chip to the concentrator  tube and attach a two-ball micro-Snyder column. Prewet the column by adding about 0.5 mL of hexane to the top. Place the micro-K-D appa- ratus on a hot water bath (60 to 65 C) so that the concentrator tube  is  partially  immersed in the hot  water.  Adjust  the  vertical  position of the apparatus and  the  water  temperature as required  to  complete  the  concentration  in 5 to 10 min. At the proper rate of distillation the balls of the column will  actively  chatter but  the  chambers  will  not  flood.  When  the

apparent volume of liquid reaches 0.5 mL, re- move the K-D apparatus  and  allow  it  to drain and cool for at least 10 min.

  - Remove the micro-Snyder column and rinse its lower joint into the concen- trator tube with  a minimum  amount of hexane. Adjust the extract volume to 1.0 mL. Stopper the concentrator tube and store re- frigerated if further processing will not be performed immediately. If the extract  will be stored longer than two days, it should be transferred to a Teflon-sealed screw-cap vial. If the sample extract requires no further cleanup, proceed with gas chromatographic analysis (Section 12). If the sample requires further cleanup, proceed to Section 11.

  - Determine the original sample vol- ume by refilling the sample bottle to the mark and transferring the liquid to  a  1000- mL graduated cylinder. Record the sample volume to the nearest 5 mL.

  - Cleanup and Separation

  - Cleanup procedures may not be nec- essary for a relatively clean sample matrix. If particular circumstances demand the use of a cleanup procedure, the analyst may use the procedure below or any other appropriate procedure. However, the analyst first must demonstrate that the requirements of Sec- tion 8.2 can be met using the method as re- vised to incorporate the cleanup procedure.

  - Florisil column cleanup:

    - Prepare a slurry of 10 g of activated Florisil in methylene chloride/hexane (1 + 9)(V/V) and place the Florisil into a chromatographic column. Tap the column to settle the Florisil and add 1 cm of anhydrous sodium sulfate to the top. Adjust the elution rate to about 2 mL/min.

    - Just prior to exposure of the sodium sulfate layer to the air,  quantitatively  trans- fer the sample extract onto the column using an additional 2 mL of hexane to complete the transfer. Just prior to exposure of the so- dium sulfate layer to the air, add 30 mL of methylene chloride/hexane (1 + 9)(V/V) and continue the elution of the column.  Discard the  eluate.

    - Next, elute the column  with  30  mL of acetone/methylene chloride (1 + 9)(V/V) into a 500-mL K-D flask equipped with a 10- mL concentrator tube. Concentrate the col- lected fraction as in Sections 10.6, 10.7, 10.8, and 10.9 including the solvent exchange to 1 mL of hexane. This fraction should  contain the nitroaromatics and isophorone. Analyze by gas chromatography (Section 12).

  - Gas Chromatography

  - Isophorone and nitrobenzene are ana- lyzed by injection of a portion of the extract into an FIDGC. The dinitrotoluenes are ana- lyzed by a separate injection into an ECDGC. Table 1 summarizes the recommended oper- ating  conditions  for  the  gas  chromatograph.

#### Pt. 136, App. A, Meth. 609

Included in this table are retention times and MDL that can be achieved under these conditions. Examples of the separations achieved by Column 1 are shown in Figures 1 and 2. Other packed or capillary (open-tubu- lar)  columns,  chromatographic  conditions, or detectors may be used if the requirements of Section 8.2 are met.

  - Calibrate the system daily as de- scribed in Section 7.

  - If the internal standard calibration procedure is being used, the internal stand- ard must be added to the same extract and mixed thoroughly immediately before injec- tion into the gas chromatograph.

  - Inject 2 to 5  L  of  the  sample  extract or  standard  into  the  gas   chromatograph using the solvent-flush  technique. 9  Smaller (1.0 L) volumes may  be  injected  if  auto- matic devices are employed. Record the vol- ume injected to the nearest 0.05 L, the total extract volume, and the  resulting  peak  size in  area  or  peak  height  units.

  - Identify the parameters in the sample by comparing the retention times of the peaks in the sample chromatogram with those of the peaks in standard chromatograms. The width of the retention time window used to make identifications should be based upon measurements of ac- tual retention time variations of standards over the course of a day. Three times the standard deviation of a retention time for a compound can be used to calculate a sug- gested window size; however, the experience of the analyst should weigh heavily in the interpretation of chromatograms.

  - If the response for a peak exceeds the working range of the system, dilute the ex- tract and reanalyze.

  - If the measurement of the peak re- sponse is prevented by the presence of inter- ferences, further cleanup is required.

  - Calculations

  - Determine the concentration of indi- vidual compounds in the sample.

    - If the external standard calibration procedure is used, calculate the amount of material injected from the peak response using the calibration curve or calibration factor determined in Section 7.2.2. The con- centration in the sample can be calculated from Equation 2.

#### 40 CFR Ch. I (7–1–17 Edition)

    - If the internal standard calibration procedure is used, calculate the concentra- tion in the sample using the response factor (RF) determined in Section 7.3.2 and Equa- tion 3.

As Is 

## Concentration (g/L) 

Ais RFVo 

Equation   3

where:

As  = Response for the parameter to be meas- ured.

Ais = Response for the internal standard.

Is   =  Amount  of  internal  standard  added  to each extract (g).

Vo = Volume of water extracted (L).

13.2 Report results in g/L without correc- tion for recovery data. All QC data obtained should be reported with the sample results.

  - Method Performance

  - The method detection limit (MDL) is defined as the minimum concentration of a substance that can be measured and reported with 99% confidence that the value is above zero. 1 The MDL concentrations listed  in Table 1 were obtained using reagent water. 10 Similar results were achieved using rep- resentative wastewaters. The MDL actually achieved in a given analysis will vary de- pending on instrument sensitivity and ma- trix  effects.

  - This method has been tested for lin- earity of spike recovery from reagent water and has been demonstrated to be applicable over the concentration range from 7 MDL to 1000 MDL. 10

  - This method was tested by 18 labora- tories using reagent water, drinking water, surface water, and three industrial wastewaters spiked at six concentrations over the range 1.0 to 515 g/L. 11 Single oper- ator precision, overall precision, and method accuracy were found to be directly related to the concentration of the parameter and es- sentially independent of the sample matrix. Linear equations to describe these relation- ships are presented in Table 3.

REFERENCES

- 40 CFR part 136, appendix B.

## Concentration (g/L) 

where:

AVt 

Vi Vs 

Equation   2

- ‘‘Determination of Nitroaromatic Com- pounds and Isophorone in Industrial and Mu- nicipal Wastewaters,’’ EPA 600/ 4–82–024, Na- tional Technical Information Service, PB82– 208398, Springfield, Virginia 22161, May 1982.

- ASTM Annual Book of Standards, Part 31, D3694–78. ‘‘Standard Practices for Prepa-

A = Amount of material injected (ng). Vi = Volume of extract injected (L). Vt = Volume of total extract (L).

Vs = Volume of water extracted (mL).

ration of Sample Containers and for Preser- vation of Organic Constituents,’’ American Society for Testing and Materials, Philadel- phia.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 609

- ‘‘Carcinogens—Working With Carcino- gens,’’ Department of Health, Education, and Welfare, Public Health Service, Center for Disease Control, National Institute for Occu- pational Safety and Health, Publication No. 77–206, August 1977.

- ‘‘OSHA Safety and Health Standards, General Industry,’’ (29 CFR part 1910), Occu- pational Safety and Health Administration, OSHA 2206 (Revised, January 1976).

- ‘‘Safety in Academic Chemistry Labora- tories,’’ American Chemical Society Publica- tion, Committee on Chemical Safety, 3rd Edition, 1979.

- Provost,  L.P.,  and  Elder,  R.S.  ‘‘Interpre- tation   of   Percent   Recovery   Data,’’   American Laboratory, 15, 58–63  (1983).  (The  value  2.44 used  in  the  equation  in  Section  8.3.3  is  two times the value 1.22 derived in this report.)

- ASTM Annual Book of Standards, Part 31, D3370–76. ‘‘Standard Practices for Sam- pling Water,’’ American Society for Testing and  Materials,  Philadelphia.

- Burke, J.A. ‘‘Gas Chromatography for Pesticide Residue Analysis; Some Practical Aspects,’’ Journal of the Association of Official Analytical Chemists, 48, 1037 (1965).

- ‘‘Determination of Method Detection Limit and Analytical Curve for EPA Method 609—Nitroaromatics and Isophorone,’’ Spe- cial letter report for EPA Contract 68–03– 2624, U.S. Environmental Protection Agency, Environmental Monitoring and Support Lab- oratory, Cincinnati, Ohio 45268, June 1980.

- ‘‘EPA Method Study 19, Method 609 (Nitroaromatics and Isophorone),’’ EPA 600/ 4–84–018, National Technical Information Service, PB84–176908, Springfield, Virginia 22161, March 1984.

TABLE 1—CHROMATOGRAPHIC CONDITIONS AND METHOD DETECTION LIMITS

| Parameter | Retention time (min) | Method detection limit (g/L) |
| --- | --- | --- |
|  | Col. 1 | Col. 2 | ECDGC | FIDGC |
| Nitrobenzene ................................................................................. | 3.31 | 4.31 | 13.7 | 3.6 |
| 2,6-Dinitrotoluene .......................................................................... | 3.52 | 4.75 | 0.01 | ¥ |
| Isophorone .................................................................................... | 4.49 | 5.72 | 15.7 | 5.7 |
| 2,4-Dinitrotoluene .......................................................................... | 5.35 | 6.54 | 0.02 | ¥ |

Column 1 conditions: Gas-Chrom Q (80/100 mesh) coated with 1.95% QF–1/1.5% OV–17 packed in a 1.2 m long 2 mm or 4 mm ID glass column. A 2 mm ID column and nitrogen carrier gas at 44 mL/min flow rate  were  used  when  determining isophorone and nitrobenzene by FIDGC. The column temperature was held isothermal at 85 C. A 4 mm ID column and 10% methane/90% argon carrier gas at 44 mL/min flow rate were used when determining the dinitrotoluenes by ECDGC. The column temperature was held isothermal at 145 C.

Column 2 conditions: Gas-Chrom Q (80/100 mesh) coated with 3% OV–101 packed in a 3.0 m long 2 mm or 4 mm ID glass

column. A 2 mm ID column and nitrogen carrier gas at 44 mL/min flow rate were used when determining isophorone and nitrobenzene by FIDGC. The column temperature was held isothermal at 100 C. A 4 mm ID column and 10% methane/90% argon carrier gas at 44 mL/min flow rate were used when determining the dinitrotoluenes by ECDGC. The column temperature was held isothermal at 150 C.

TABLE 2—QC ACCEPTANCE CRITERIA—METHOD 609

| Parameter | Test Conc. (g/L) | Limit for s (g/L) | Range for X¯ (g/L) | Range for P, Ps (%) |
| --- | --- | --- | --- | --- |
| 2,4-Dinitrotoluene .............................................................................. | 20 | 5.1 | 3.6–22.8 | 6–125 |
| 2,6-Dinitrotoluene .............................................................................. | 20 | 4.8 | 3.8–23.0 | 8–126 |
| Isophorone ........................................................................................ | 100 | 32.3 | 8.0–100.0 | D–117 |
| Nitrobenzene ..................................................................................... | 100 | 33.3 | 25.7–100.0 | 6–118 |

s = Standard deviation of four recovery measurements, in g/L (Section 8.2.4). X¯ = Average recovery for four recovery measurements, in g/L (Section 8.2.4).

P, Ps  = Percent recovery measured (Section 8.3.2, Section 8.4.2). D = Detected; result must be greater than zero.

NOTE: These criteria are based directly upon the method performance data in Table 3. Where necessary, the limits for recov- ery have been broadened to assure applicability of the limits to concentrations below those used to develop Table 3.

TABLE 3—METHOD ACCURACY AND PRECISION AS FUNCTIONS OF CONCENTRATION—METHOD 609

| Parameter | Accuracy, as re- covery, X(g/L) | Single analyst pre- cision, sr(g/L) | Overall precision, S(g/L) |
| --- | --- | --- | --- |
| 2,4-Dinitro- toluene ......................................................................................... 2,6-Dinitro- toluene ......................................................................................... Isophorone ....................................................................................... Nitrobenzene ................................................................................... | 0.65C + 0.22 0.66C + 0.20 0.49C + 2.93 0.60C + 2.00 | 0.20X¯ + 0.08 0.19X¯ + 0.06 0.28X¯ + 2.77 0.25X¯ + 2.53 | 0.37X¯ ¥0.07 0.36X¯ ¥0.00 0.46X¯ + 0.31 0.37X¯ ¥0.78 |

X= Expected recovery for one or more measurements of a sample containing a concentration of C, in g/L.

sr= Expected single analyst standard deviation of measurements at an average concentration found of X¯ , in g/L. S= Expected interlaboratory standard deviation of measurements at an average concentration found of X¯ , in g/L. C = True value for the concentration, in g/L.

X¯ = Average recovery found for measurements of samples containing a concentration of C, in g/L.

#### Pt. 136, App. A, Meth. 609

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 609

Pt. 136, App. A, Meth. 610

METHOD 610—POLYNUCLEAR AROMATIC HYDROCARBONS

- Scope and Application

  - This method covers the determination of certain polynuclear aromatic hydro- carbons (PAH). The following parameters can be determined by this method:

| Parameter | STORET No. | CAS No. |
| --- | --- | --- |
| Acenaphthene ....................... | 34205 | 83–32–9 |
| Acenaphthylene ..................... | 34200 | 208–96–8 |
| Anthracene ............................ | 34220 | 120–12–7 |
| Benzo(a)anthracene .............. | 34526 | 56–55–3 |
| Benzo(a)pyrene ..................... | 34247 | 50–32–8 |
| Benzo(b)fluoranthene ............ | 34230 | 205–99–2 |
| Benzo(ghi)perylene ................ | 34521 | 191–24–2 |
| Benzo(k)fluoranthene ............ | 34242 | 207–08–9 |
| Chrysene ............................... | 34320 | 218–01–9 |
| Dibenzo(a,h)anthracene ........ | 34556 | 53–70–3 |
| Fluoranthene .......................... | 34376 | 206–44–0 |
| Fluorene ................................. | 34381 | 86–73–7 |
| Indeno(1,2,3-cd)pyrene ......... | 34403 | 193–39–5 |
| Naphthalene .......................... | 34696 | 91–20–3 |
| Phenanthrene ........................ | 34461 | 85–01–8 |
| Pyrene ................................... | 34469 | 129–00–0 |

  - This is a chromatographic method ap- plicable to the determination of the com- pounds listed above in municipal and indus- trial  discharges  as  provided  under  40  CFR

136.1. When this method is used to analyze unfamiliar samples for any or all of the com- pounds  above,  compound  identifications should be supported by  at  least  one  addi- tional qualitative technique. Method 625 pro- vides gas chromatograph/mass spectrometer (GC/MS) conditions appropriate for the qual- itative and quantitative confirmation  of  re- sults  for  many  of  the  parameters  listed above, using the extract produced by this method.

  - This method provides for both high performance liquid chromatographic (HPLC) and gas  chromatographic  (GC)  approaches for the determination of PAHs. The gas chromatographic procedure does not ade- quately resolve the following four pairs of compounds: Anthracene and phenanthrene; chrysene	and	benzo(a)anthracene; benzo(b)fluoranthene		and benzo(k)fluoranthene; and dibenzo(a,h) an- thracene and indeno (1,2,3-cd)pyrene. Unless the purpose for the analysis can be served by reporting the sum of an unresolved pair, the liquid chromatographic approach must be used for these compounds. The liquid chromatographic method does resolve all 16 of the PAHs listed.

  - The method detection limit (MDL, de- fined in Section 15.1) 1 for each parameter is listed in Table 1. The MDL for a specific wastewater may differ from those listed, de- pending upon the nature of interferences  in the sample matrix.

  - The sample extraction and  concentra- tion steps in this method are essentially the same as in Methods 606, 608, 609, 611, and 612.

#### 40 CFR Ch. I (7–1–17 Edition)

Thus, a single sample may be extracted to measure the parameters included in the scope of each of these methods. When clean- up is required, the concentration levels must be high  enough  to  permit  selecting  aliquots, as necessary, to apply appropriate cleanup procedures. Selection of the aliquots must be made prior to the solvent exchange steps of this method. The analyst is allowed the lati- tude, under Sections 12 and 13, to select chromatographic conditions appropriate for the simultaneous measurement of combina- tions of these parameters.

  - Any modification of this method,  be- yond those expressly permitted, shall be con- sidered as a major modification subject to application and approval of alternate test procedures under 40 CFR 136.4 and 136.5.

  - This method is restricted to use by or under the supervision of analysts experi- enced in  the use of HPLC and  GC systems and in the interpretation of liquid and gas chromatograms. Each  analyst must  dem- onstrate the ability to generate acceptable results with this method using the procedure described in Section 8.2.

- Summary of Method

  - A measured volume of sample, ap- proximately 1–L, is extracted with  meth- ylene chloride using a separatory funnel. The methylene chloride extract is dried and con- centrated to a volume of 10 mL or less. The extract is then separated by HPLC or GC. Ul- traviolet (UV) and fluorescence detectors are used with HPLC to identify and measure the PAHs. A flame ionization detector is used with GC. 2

  - The method provides a silica gel col- umn cleanup procedure to aid in the elimi- nation of interferences that may be encoun- tered.

- Interferences

  - Method interferences may be caused by contaminants in solvents, reagents, glass- ware, and other sample processing hardward that lead to discrete artifacts and/or ele- vated baselines in the chromatograms. All of these materials must be routinely dem- onstrated to be free from interferences under the conditions of the analysis by running laboratory reagent blanks as described in Section 8.1.3.

    - Glassware must be scrupulously cleaned. 3 Clean all glassware as soon as pos- sible after use by rinsing with the last  sol- vent used in it. Solvent rinsing should be fol- lowed by detergent washing with hot water, and rinses with tap water and distilled water. The glassware should then be drained dry, and heated in a muffle furnace at 400 C for 15 to 30 min. Some thermally stable ma- terials, such as PCBs, may not be eliminated by this treatment. Solvent rinses with ace- tone  and  pesticide  quality  hexane  may  be

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 610

substituted for the muffle furnace heating. Thorough rinsing with such solvents usually eliminates PCB interference. Volumetric ware should not be heated in a muffle fur- nace. After drying and cooling, glassware should be sealed and stored in a clean envi- ronment to prevent any accumulation of dust or other contaminants. Store inverted or capped with aluminum foil.

    - The use of high purity reagents and solvents helps to minimize interference prob- lems. Purification of solvents  by  distillation in all-glass systems may be required.

  - Matrix interferences may be caused by contaminants that are co-extracted from the sample. The extent of matrix interferences will vary considerably from source to source, depending upon the nature and diversity  of the industrial complex or municipality being sampled.  The  cleanup  procedure  in  Section

11 can be used to overcome many of these interferences, but unique samples may re- quire additional cleanup approaches to achieve the MDL listed in Table 1.

  - The extent of interferences that may be encountered using liquid chromatographic techniques has not been fully assessed. Al- though the HPLC conditions described allow for a unique resolution of the specific PAH compounds covered by this method, other PAH compounds may interfere.

- Safety

  - The   toxicity   or   carcinogenicity   of each reagent used in this method have not been precisely defined; however, each chem- ical compound should be treated as a poten- tial health hazard. From this viewpoint, ex- posure to these chemicals must be reduced to the lowest possible level by whatever means available. The laboratory is responsible for maintaining   a   current   awareness   file   of OSHA  regulations  regarding  the  safe  han- dling of the chemicals specified in this meth- od. A reference file of material data handling sheets should also be made available to all personnel involved in the chemical analysis. Additional  references  to  laboratory  safety are available and have been identified 4M6 for the information of the analyst.

  - The following parameters covered by this method have been  tentatively  classified as known or suspected, human or mamma- lian	carcinogens:	benzo(a)anthracene, benzo(a)pyrene, and dibenzo(a,h)-anthracene. Primary standards of these toxic compounds should be prepared in a hood. A NIOSH/ MESA approved toxic gas respirator  should be worn when the analyst handles high con- centrations of these toxic compounds.

- Apparatus and Materials

  - Sampling equipment, for discrete or composite  sampling.

    - Grab sample bottle—1–L or 1-qt, amber  glass,  fitted  with  a  screw  cap  lined

with Teflon. Foil may be substituted for Tef- lon if the sample is not corrosive. If amber bottles are not available, protect samples from light. The bottle and cap liner must be washed, rinsed with acetone or methylene chloride, and dried before use to minimize contamination.

    - Automatic sampler (optional)—The sampler must incorporate glass sample con- tainers for the collection of a minimum of 250 mL of sample. Sample containers must be kept refrigerated at 4 C and protected from light during compositing. If the sampler uses a peristaltic pump, a minimum length of compressible silicone rubber tubing may be used. Before use, however, the compressible tubing should be thoroughly rinsed with methanol, followed by repeated rinsings with distilled water to minimize the potential for contamination of the sample. An integrating flow meter is required to collect flow propor- tional  composites.

  - Glassware (All specifications are sug- gested. Catalog numbers are included for il- lustration only.):

    - Separatory funnel—2–L, with Teflon stopcock.

    - Drying column—Chromatographic column, approximately 400 mm long 19 mm ID,  with  coarse  frit  filter  disc.

    - Concentrator tube, Kuderna-Dan- ish—10-mL, graduated (Kontes K–570050–1025 or equivalent). Calibration must  be  checked at the volumes employed in the test. Ground glass stopper is used to prevent evaporation of  extracts.

    - Evaporative flask, Kuderna-Danish— 500-mL (Kontes K–570001–0500 or equivalent). Attach  to  concentrator  tube  with  springs.

    - Snyder column, Kuderna-Danish— Three-ball macro (Kontes K–503000–0121 or equivalent).

    - Snyder column, Kuderna-Danish— Two-ball micro (Kontes K–569001–0219 or equivalent).

    - Vials—10 to 15-mL, amber glass, with Teflon-lined screw cap.

    - Chromatographic column—250 mm long 10 mm ID, with coarse frit filter disc at bottom and Teflon stopcock.

  - Boiling chips—Approximately 10/40 mesh. Heat to 400 C for 30 min or Soxhlet ex- tract  with  methylene  chloride.

  - Water bath—Heated, with concentric ring cover, capable of temperature control (2 C). The bath should be used in a hood.

  - Balance—Analytical, capable of accu- rately weighing 0.0001 g.

  - High performance liquid chro- matograph (HPLC)—An analytical system complete with column supplies, high pres- sure syringes, detectors, and compatible strip-chart recorder. A data system is rec- ommended for measuring peak areas and re- tention times.

    - Gradient pumping system—Constant flow.

#### Pt. 136, App. A, Meth. 610

    - Reverse phase column—HC-ODS Sil- X, 5 micron particle diameter, in a 25 cm 

2.6 mm ID  stainless  steel column  (Perkin Elmer No. 089–0716 or equivalent). This col- umn was used to develop the method per- formance statements in Section 15. Guide- lines for the use of  alternate  column packings are provided in Section 12.2.

5.6.3 Detectors—Fluorescence and/or UV detectors. The fluorescence detector is used for excitation at 280 nm and emission greater than 389 nm cutoff (Corning 3–75 or equiva- lent). Fluorometers should have dispersive optics for excitation  and  can  utilize  either filter or dispersive optics at the emission de- tector. The UV detector is used at  254  nm and should be coupled to the fluorescence de- tector. These detectors were used to  develop the method performance statements in Sec- tion 15. Guidelines for the use of alternate detectors are provided in Section 12.2.

  - Gas chromatograph—An analytical system complete with temperature program- mable gas chromatograph suitable for on- column or splitless injection and all required accessories including syringes, analytical columns, gases, detector, and strip-chart re- corder. A data system is recommended for measuring peak areas.

    - Column—1.8 m long 2 mm ID glass,

packed with 3% OV–17 on Chromosorb W-AW- DCMS (100/120 mesh) or equivalent. This col- umn was used to develop the retention time data in Table 2. Guidelines for the use of al- ternate column packings are provided in Section 13.3.

    - Detector—Flame ionization detector. This detector has proven effective in the analysis of wastewaters for the parameters listed in the scope (Section 1.1), excluding the four pairs of unresolved compounds list- ed in Section 1.3. Guidelines for the use of al- ternate detectors are provided in Section 13.3.

- Reagents

  - Reagent water—Reagent water is de- fined as a water in which an  interferent  is not observed at the  MDL  of  the  parameters of  interest.

  - Sodium thiosulfate—(ACS) Granular.

  - Cyclohexane, methanol, acetone, methylene chloride, pentane—Pesticide qual- ity or equivalent.

  - Acetonitrile—HPLC quality,  distilled in glass.

  - Sodium sulfate—(ACS) Granular, an- hydrous. Purify by heating at 400 C for 4 h in a shallow tray.

  - Silica gel—100/200 mesh, desiccant, Davison, grade-923 or equivalent. Before use, activate for at least 16 h at 130 C in a shal- low glass tray, loosely covered with foil.

  - Stock standard solutions (1.00 g/L)—

Stock standard solutions can be prepared from pure standard materials or purchased as certified solutions.

#### 40 CFR Ch. I (7–1–17 Edition)

    - Prepare stock  standard solutions by accurately weighing about 0.0100 g of pure material. Dissolve the  material  in  acetoni- trile and dilute to volume in a 10-mL volu- metric flask. Larger volumes can be  used  at the convenience of the analyst. When com- pound purity is assayed to be 96% or greater, the weight can be used without correction to calculate the concentration of the stock standard. Commercially prepared stock standards can be  used  at  any  concentration if they are certified  by  the  manufacturer  or by an independent source.

    - Transfer the stock standard solu- tions into Teflon-sealed screw-cap bottles. Store at 4 C and protect from light. Stock standard solutions should be checked fre- quently for signs of degradation or evapo- ration, especially just prior to preparing calibration standards from them.

    - Stock standard solutions must be re- placed after six months, or sooner if com- parison with check standards indicates a problem.

6.8 Quality control check sample con- centrate—See Section 8.2.1.

- Calibration

  - Establish	liquid	or	gas chromatographic operating conditions equiv- alent to those given in Table 1 or 2. The chromatographic system can be calibrated using the external standard technique (Sec- tion 7.2) or the internal standard technique (Section 7.3).

  - External standard calibration proce- dure:

    - Prepare calibration standards at a minimum of three concentration levels  for each parameter of interest by adding vol- umes of one or more stock standards to a volumetric flask and diluting to volume with acetonitrile. One of the external standards should be at a concentration near, but above, the MDL (Table 1) and the other concentra- tions should correspond to the expected range of concentrations found in real sam- ples or should define the working range of the detector.

    - Using injections of 5 to 25 L for HPLC and 2 to 5 L for GC, analyze each cali- bration standard  according  to Section  12  or 13, as appropriate. Tabulate peak height or area responses against  the  mass  injected. The results can be used to prepare a calibra- tion curve for each compound. Alternatively,

if the ratio of response to amount injected (calibration factor) is a constant over the working range (<10% relative standard devi- ation, RSD), linearity through the origin can be assumed and the average ratio or calibra- tion factor can be used in place of a calibra- tion curve.

  - Internal standard calibration proce- dure—To use this approach, the analyst must select one or more internal standards that are  similar  in  analytical  behavior  to  the

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 610

compounds of interest. The analyst must fur- ther demonstrate that the measurement of the internal standard is not affected by method or matrix interferences. Because of these limitations, no internal standard  can be suggested that is applicable to all sam- ples.

    - Prepare calibration standards at a minimum of three concentration levels  for each parameter of interest by adding vol- umes of one or more stock standards to a volumetric flask. To each calibration stand- ard, add a known constant amount of one or more internal standards, and dilute to vol- ume with acetonitrile. One of the standards should be at a concentration near, but above, the MDL and the other concentrations should correspond to the expected range of concentrations found in real samples or should define the working range of the detec- tor.

    - Using injections of 5  to  25  L  for HPLC and 2 to 5 L for GC, analyze each cali- bration standard according to Section  12  or 13, as appropriate. Tabulate peak height or area  responses  against  concentration  for each compound and internal standard. Cal- culate response factors (RF) for each  com- pound using  Equation 1.

As Cis 

## RF 

Ais Cs 

Equation   1

where:

As  = Response for the parameter to be meas- ured.

Ais = Response for the internal standard.

Cis  = Concentration of the internal standard (g/L).

Cs   =  Concentration  of  the  parameter  to  be measured (g/L).

If the RF value over the working range is a constant (<10% RSD), the RF can be assumed to be invariant and the average RF can be used for calculations. Alternatively, the re- sults can be used to plot a calibration curve of response ratios, As/Ais, vs. RF.

  - The working calibration curve, cali- bration factor, or RF must be verified on each working day by the measurement of one or more calibration standards. If the re- sponse for any parameter varies from the predicted response by more than 15%, the test must be repeated using a  fresh calibra- tion standard. Alternatively, a new calibra- tion curve must be prepared for that com- pound.

  - Before using any cleanup procedure, the analyst must process a series of calibra- tion standards through the procedure to vali- date elution patterns and the absence of interferences from the reagents.

- Quality Control

  - Each laboratory that uses this method is required to operate a formal quality  con- trol program. The minimum requirements of this program consist of an initial demonstra- tion of laboratory capability and an ongoing analysis of spiked samples to evaluate and document data quality. The laboratory must maintain records to document the quality of data that is generated. Ongoing data quality checks are compared with established per- formance criteria to determine if the results of analyses meet the performance character- istics of the method. When results of sample spikes indicate atypical method perform- ance, a quality control check  standard  must be analyzed to confirm that the measure- ments were performed in an in-control mode of operation.

    - The analyst must make an initial, one-time, demonstration of the ability to generate acceptable accuracy and precision with this method. This  ability  is  established as described in Section 8.2.

    - In recognition of advances that are occurring in chromatography, the analyst is permitted certain options (detailed in Sec- tions 10.4, 11.1, 12.2, and 13.3) to improve the separations or lower the cost of measure- ments. Each time such a  modification  is made to the method, the analyst is required to repeat the procedure in Section 8.2.

    - Before processing any samples the analyst must analyze a  reagent  water  blank to demonstrate that interferences from the analytical system and glassware are under control. Each time a set of samples is ex- tracted or reagents are changed a reagent water blank must be processed as a safe- guard  against  laboratory  contamination.

    - The laboratory must, on an ongoing basis, spike and analyze a minimum of 10% of all samples to monitor and evaluate lab- oratory data quality. This procedure is de- scribed in Section 8.3.

    - The laboratory must, on an ongoing basis, demonstrate through the analyses of quality control  check standards  that  the op- eration of the measurement system is in con- trol.  This  procedure  is  described  in  Section

8.4. The frequency of the check standard analyses is equivalent to 10% of all samples analyzed but may be reduced if spike recov- eries from samples (Section 8.3) meet all specified quality control criteria.

    - The laboratory must maintain per- formance records to document the quality of data that is generated. This procedure is de- scribed in Section 8.5.

  - To establish the ability to generate acceptable accuracy and precision, the ana- lyst must perform the following operations.

    - A quality control (QC) check sample concentrate is required containing each pa- rameter of interest at the following con- centrations in acetonitrile: 100 g/mL of any

#### Pt. 136, App. A, Meth. 610

of the six early-eluting PAHs (naphthalene, acenaphthylene, acenaphthene, fluorene, phenanthrene, and anthracene); 5 g/mL of benzo(k)fluoranthene; and 10 g/mL of any of the other PAHs. The QC check sample con- centrate must be obtained from the U.S. En- vironmental Protection Agency, Environ- mental Monitoring and Support  Laboratory in Cincinnati, Ohio, if available. If not avail- able from that source, the QC check sample concentrate must be obtained from another external source. If not available from either source above, the QC check sample con- centrate must be prepared by the laboratory using stock standards prepared independ- ently from those used for calibration.

    - Using a pipet, prepare QC check sam- ples at the test concentrations  shown  in Table 3 by adding 1.00 mL  of  QC  check  sam- ple concentrate to each  of  four  1–L  aliquots of  reagent  water.

    - Analyze the well-mixed QC check samples according to the  method  beginning in Section 10.

    - Calculate the average recovery (X¯ ) in

g/L, and the standard deviation of the re- covery (s) in g/L, for each parameter using the four results.

    - For each parameter compare s and X¯

with the corresponding acceptance criteria for   precision   and   accuracy,   respectively,

found in Table 3. If s and X¯  for all param-

eters of interest meet the acceptance cri- teria, the system performance is acceptable and analysis of actual samples can begin. If any individual s exceeds the precision limit

or any individual X¯  falls outside the range

for accuracy, the system performance is un- acceptable for that parameter.

NOTE: The large number of parameters in Table 3 present  a  substantial  probability that one or more will fail at least one of the acceptance criteria when all parameters are analyzed.

    - When one or more of the parameters tested fail at least one of the acceptance cri- teria, the analyst must proceed according to Section 8.2.6.1 or 8.2.6.2.

      - Locate and correct the source of the problem and repeat the test for all pa- rameters of interest beginning with Section 8.2.2.

      - Beginning with Section 8.2.2, repeat the test only for those  parameters  that failed to meet criteria. Repeated failure, however, will confirm a  general  problem with the measurement system. If this occurs, locate and correct the source of the problem and repeat the test for all compounds of in- terest beginning with Section 8.2.2.

8.3 The laboratory must, on an ongoing basis, spike at least 10% of the samples from each sample site being monitored to assess accuracy. For laboratories analyzing one to ten samples per month, at least one spiked sample per month is required.

#### 40 CFR Ch. I (7–1–17 Edition)

    - The concentration of the spike in the sample should be determined as follows:

      - If, as in compliance monitoring, the concentration of a specific parameter in the sample is being checked against a regu- latory concentration limit, the spike should be at that limit or 1 to 5 times higher than the background concentration determined in Section 8.3.2, whichever concentration would be larger.

      - If the concentration of a specific parameter in the sample  is  not  being checked against a limit specific to that pa- rameter, the spike should be at the test con- centration in Section 8.2.2 or 1 to 5 times higher than the background concentration determined in Section 8.3.2, whichever con- centration would be larger.

      - If it is impractical to determine background levels before spiking (e.g., max- imum holding times will be exceeded), the spike concentration should be (1) the regu- latory concentration limit, if any;  or,  if none, (2) the larger of either 5 times higher than the expected background concentration or the test concentration in Section 8.2.2.

    - Analyze one sample aliquot to deter- mine the background concentration (B) of each parameter. If necessary, prepare a new QC check sample concentrate (Section 8.2.1) appropriate for the background concentra- tions in the sample. Spike a second sample aliquot with 1.0 mL of the QC check sample concentrate and analyze it to determine the concentration after spiking (A) of each pa- rameter. Calculate each percent recovery (P) as 100 (A¥B)%/T, where T is the known true value of the spike.

    - Compare the percent recovery (P) for each parameter with the corresponding QC acceptance criteria found in Table 3. These acceptance criteria were calculated to  in- clude an allowance for error in measurement of both the background and spike concentra- tions, assuming a spike  to  background  ratio of 5:1. This error will be accounted for to the extent that the analyst’s spike to back- ground ratio approaches 5:1. 7 If spiking was performed at a concentration lower than the test concentration in Section 8.2.2, the ana- lyst must use either the QC acceptance cri- teria in Table 3, or optional QC acceptance criteria calculated for the specific spike con- centration. To calculate optional acceptance criteria for the recovery of a parameter: (1) Calculate accuracy (X) using the equation in Table 4, substituting the spike concentration

(T) for C; (2) calculate overall precision (S) using the equation in Table 4, substituting X for X¯ ; (3) calculate the range for recovery at

the spike concentration as (100 X/T)2.44(100 S/T)%. 7

    - If any individual P falls outside the designated range for recovery, that param- eter has failed the acceptance criteria. A check  standard  containing  each  parameter

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 610

that failed the critiera must be analyzed as described in Section 8.4.

  - If any parameter fails the acceptance criteria for recovery in Section 8.3, a QC check standard containing each parameter that failed must be prepared and analyzed.

NOTE: The frequency for the required anal- ysis of a QC check standard will depend upon the number of parameters being simulta- neously tested, the complexity of the sample matrix, and the performance of the labora- tory. If the entire list of parameters in Table 3 must be measured in the sample in Section 8.3, the probability that the analysis of a QC check standard will be required is high.  In this case the QC check standard should be routinely analyzed with the spike sample.

    - Prepare the QC check standard by adding 1.0 mL of QC check sample con- centrate (Section 8.2.1 or 8.3.2) to 1 L of rea- gent water. The QC check standard needs only to contain the parameters that failed criteria in the test in Section 8.3.

    - Analyze the QC check standard to determine the concentration measured (A) of each parameter. Calculate each percent re- covery (Ps) as 100 (A/T)%, where T is the true value of the standard concentration.

    - Compare the percent recovery (Ps) for each parameter with the corresponding QC acceptance criteria found in Table 3. Only parameters that failed the test in Section 8.3 need to be compared with these  criteria.  If the recovery of any such parameter falls out- side the designated range, the laboratory performance for that parameter is judged to be out of control, and the problem must be immediately identified and corrected. The analytical result for that parameter in the unspiked sample is suspect  and may not  be reported for regulatory compliance purposes.

  - As part of the QC program for the lab- oratory, method accuracy for wastewater samples must be assessed and records must be maintained. After the analysis of five spiked wastewater samples as in Section 8.3,

calculate  the  average  percent  recovery  (P¯ )

and the standard deviation of the percent re- covery (sp). Express the accuracy assessment

as a percent recovery interval from P¯ –2sp to P¯ + 2sp. If P¯ = 90% and sp = 10%, for example,

the accuracy interval is expressed as 70– 110%. Update the accuracy  assessment  for each parameter on a regular basis (e.g. after each five to  ten  new  accuracy  measure- ments).

  - It is recommended that the laboratory adopt additional quality assurance practices for use  with  this method.  The  specific  prac- tices that  are  most  productive  depend  upon the needs of the laboratory and the nature of the samples. Field duplicates may be ana- lyzed to assess the precision of the environ- mental measurements. When doubt exists over the identification of a peak on the chro- matogram, confirmatory techniques such as gas  chromatography  with  a  dissimilar  col-

umn, specific element detector, or mass spectrometer must be used. Whenever pos- sible, the laboratory should analyze standard reference materials and participate in rel- evant performance evaluation studies.

- Sample Collection, Preservation, and Handling

  - Grab samples must be collected  in glass containers. Conventional sampling practices 8 should be followed, except  that the bottle must not be prerinsed with sample before collection. Composite samples should be collected in refrigerated  glass  containers in accordance with the requirements of the program. Automatic sampling equipment must be as free as possible of Tygon tubing and other potential sources of contamina- tion.

  - All samples must be iced or refrig- erated at 4 C from the time of collection until extraction. PAHs are known to be light sensitive; therefore, samples, extracts, and standards should be stored in amber or foil- wrapped bottles in order to minimize photo- lytic decomposition. Fill the sample bottles and, if residual chlorine is present, add 80 mg of sodium thiosulfate per liter of sample and mix well. EPA Methods 330.4 and 330.5 may be used for measurement of residual chlo- rine. 9 Field test kits are available for this purpose.

  - All samples must be extracted within 7 days of collection and completely analyzed within 40 days of extraction. 2

- Sample Extraction

  - Mark the water meniscus on the side of the sample bottle for later determination of sample volume. Pour the entire sample into a 2–L separatory funnel.

  - Add 60 mL of methylene chloride  to the sample bottle, seal, and shake 30 s to rinse the inner surface. Transfer the solvent to the separatory funnel and extract the sample by shaking the funnel for 2 min. with periodic venting to release excess pressure. Allow the organic layer to separate from the water phase for a minimum of 10 min. If the emulsion interface between layers is more than one-third the volume of  the  solvent layer, the analyst must employ mechanical techniques to complete the phase separation. The optimum technique depends upon the sample, but may include  stirring,  filtration of the emulsion through glass wool, cen- trifugation, or other physical methods. Col- lect the methylene chloride extract in a 250– mL  Erlenmeyer  flask.

  - Add a second 60-mL volume of meth- ylene chloride to the sample bottle and re- peat the extraction procedure a second time, combining the extracts in the Erlenmeyer flask. Perform a third extraction in the same manner.

#### Pt. 136, App. A, Meth. 610

  - Assemble a Kuderna-Danish (K-D) concentrator by attaching a 10-mL concen- trator tube to a 500-mL evaporative flask. Other concentration devices or  techniques may be used in place of the K-D concentrator if the requirements of Section 8.2 are met.

  - Pour the combined extract through a solvent-rinsed drying column containing about 10 cm of anhydrous sodium sulfate, and collect the extract in the K-D concen- trator. Rinse the Erlenmeyer flask and col- umn with 20 to 30 mL of methylene chloride to complete the quantitative transfer.

  - Add one or two clean boiling chips to the evaporative flask and attach a three-ball Snyder column. Prewet the Snyder  column by adding about 1 mL of methylene chloride to the top. Place the K-D apparatus on a hot water bath (60 to 65 C) so that the concen- trator tube is partially immersed in the hot water, and the entire lower rounded surface of the flask is bathed with hot vapor. Adjust the vertical position of the apparatus  and the water temperature as required to com- plete the concentration in 15 to  20  min.  At the proper rate of distillation the balls of the column will actively chatter but the cham- bers will not flood with condensed solvent. When the apparent volume of liquid reaches 1 mL, remove the K-D apparatus and allow it to drain and cool for at least 10 min.

  - Remove the Snyder column and rinse the flask and its lower joint into the concen- trator tube with 1 to 2 mL of methylene chloride. A 5-mL syringe is recommended for this  operation.  Stopper  the  concentrator tube and store refrigerated if further proc- essing will not be performed immediately. If the extract will be stored longer than two days, it should be transferred to a Teflon- sealed screw-cap vial and protected  from light. If the sample extract requires no fur- ther cleanup, proceed with gas or liquid chromatographic analysis (Section 12 or 13). If the sample requires further cleanup, pro- ceed to Section 11.

  - Determine the original sample vol- ume by refilling the sample bottle to the mark and transferring the liquid to  a  1000- mL graduated cylinder. Record the sample volume to the nearest 5 mL.

- Cleanup and Separation

  - Cleanup procedures may not be nec- essary for a relatively clean sample matrix. If particular circumstances demand the use of a cleanup procedure, the analyst may use the procedure below or any other appropriate procedure. However, the analyst first must demonstrate that the requirements of Sec- tion 8.2 can be met using the methods as re- vised to incorporate the cleanup procedure.

  - Before the silica gel cleanup tech- nique can be utilized,  the  extract  solvent must be exchanged to cyclohexane. Add 1 to

10  mL  of  the  sample  extract  (in  methylene chloride)  and  a  boiling  chip  to  a  clean  K-D

#### 40 CFR Ch. I (7–1–17 Edition)

concentrator tube. Add 4 mL of cyclohexane and attach a two-ball micro-Snyder column. Prewet the column by adding 0.5 mL of methylene chloride to the top. Place the micro-K-D apparatus on a boiling (100 C) water bath so that the concentrator tube is partially immersed in the hot water.  Adjust the vertical position of the apparatus  and the water temperature as required to com- plete concentration in 5 to 10 min. At the proper rate of distillation the balls of the column will actively chatter but the cham- bers will not flood. When the apparent vol- ume of the liquid reaches 0.5 mL, remove the K-D apparatus and allow it to drain and cool for at least 10 min. Remove the  micro-Sny- der column and rinse its lower joint into the concentrator tube with a  minimum  amount of cyclohexane. Adjust the extract volume to about 2 mL.

  - Silica gel column cleanup for PAHs:

    - Prepare a slurry of 10 g of activiated silica gel in methylene chloride and place this into a 10-mm ID chromatographic col- umn. Tap the column to settle the  silica  gel and elute the methylene chloride. Add 1 to 2 cm of anhydrous sodium sulfate to the top of the  silica  gel.

    - Preelute the  column with  40 mL  of pentane. The rate for all elutions should be about 2 mL/min. Discard the eluate and just prior to exposure of the sodium sulfate layer to the air, transfer the 2-mL cyclohexane sample extract onto the column using an ad- ditional 2 mL cyclohexane to complete the transfer. Just prior to exposure of the so- dium sulfate layer to the air, add 25 mL of pentane and continue the elution of the col- umn. Discard this pentane eluate.

    - Next, elute the column  with  25  mL of methylene chloride/pentane (4 + 6)(V/V) into a 500-mL K-D flask equipped with a 10- mL concentrator tube. Concentrate the col- lected fraction to less than 10 mL as in Sec- tion 10.6. When the apparatus is cool, remove the Snyder column and rinse  the  flask  and its lower joint with pentane. Proceed with HPLC  or  GC  analysis.

- High Performance Liquid Chromatography

  - To the extract in the  concentrator tube, add 4 mL of acetonitrile and a new boiling chip, then attach a two-ball micro- Snyder column. Concentrate the  solvent  as in Section 10.6, except set the water bath at 95 to 100 C. When the apparatus is cool, re- move the micro-Snyder column and rinse its lower joint into the concentrator tube with about 0.2 mL of acetonitrile. Adjust the ex- tract volume to 1.0 mL.

  - Table 1 summarizes the recommended operating conditions for the  HPLC.  Included in this table are retention times, capacity factors, and MDL that can be achieved under these conditions. The UV detector is rec- ommended for the determination of naph- thalene,   acenaphthylene,   acenapthene,   and

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 610

fluorene and the fluorescence detector is rec- ommended for the remaining PAHs. Exam- ples of the separations achieved  by  this HPLC column are shown in Figures 1 and 2. Other HPLC columns, chromatographic con- ditions, or detectors may be used if the re- quirements of Section 8.2 are met.

  - Calibrate the system daily as de- scribed in Section 7.

  - If the internal standard calibration procedure is being used, the internal stand- ard must be added to the sample extract and mixed thoroughly immediately before injec- tion into the instrument.

  - Inject 5 to 25 L of the sample extract

or standard into the HPLC using a high  pres- sure syringe or a constant volume sample in- jection loop. Record the volume injected  to the  nearest  0.1  L,  and  the  resulting   peak size in area or peak height units. Re-equili- brate the HPLC  column  at  the  initial  gra- dient conditions for at least 10 min between injections.

  - Identify the parameters in the sample by comparing  the retention  time of  the peaks in the sample chromatogram with those of the peaks in standard chromatograms. The width of the retention time window used to make identifications should be based upon measurements of ac- tual retention time variations of standards over the course of a day. Three times the standard deviation of a retention time for a compound can be used to calculate a sug- gested window size; however, the experience of the analyst should weigh heavily in the interpretation of chromatograms.

  - If the response for a peak exceeds the working range of the system, dilute the ex- tract with acetonitrile and reanalyze.

  - If the measurement of the peak re- sponse is prevented by the presence of inter- ferences, further cleanup is required.

- Gas Chromatography

  - The packed column GC procedure will not resolve certain isomeric pairs as indi- cated in Section 1.3 and Table 2. The liquid chromatographic procedure (Section 12) must be used for these parameters.

  - To achieve maximum sensitivity with this method, the extract must be con- centrated to 1.0 mL. Add a clean boiling chip to the methylene chloride extract in the con- centrator tube. Attach a two-ball micro-Sny- der column. Prewet the micro-Snyder col- umn by adding about 0.5 mL of methylene chloride to the top. Place the micro-K-D ap- paratus on a hot water bath (60 to 65 C) so that the concentrator tube is partially im- mersed in the hot water. Adjust the vertical position of the apparatus and the water tem- perature as required to complete the con- centration in 5 to 10 min. At the proper rate of distillation the balls will actively  chatter but the chambers will not flood. When the apparent volume of liquid reaches 0.5 mL, re-

move the K-D apparatus  and  allow  it  to drain and cool for at least  10  min.  Remove the micro-Snyder column and rinse its lower joint into the concentrator tube with a min- imum amount of methylene chloride. Adjust the final volume to 1.0 mL and stopper the concentrator   tube.

  - Table 2 summarizes the recommended operating conditions for the gas chro- matograph. Included in this table are reten- tion times that were obtained under these conditions. An example of the separations achieved  by  this  column  is  shown  in  Figure

3. Other packed or capillary (open-tubular) columns, chromatographic conditions, or de- tectors may be used if the requirements of Section 8.2 are met.

  - Calibrate the gas chromatographic system daily as described in Section 7.

  - If the internal standard calibration procedure is being used, the internal stand- ard must be added to the sample extract and mixed thoroughly immediately before injec- tion into the gas chromatograph.

  - Inject 2 to 5  L  of  the  sample  extract or  standard  into  the  gas   chromatograph using the solvent-flush  technique. 10  Smaller (1.0 L) volumes may  be  injected  if  auto- matic devices are employed. Record the vol- ume injected to the nearest 0.05 L, and the resulting peak size in  area  or  peak  height units.

  - Identify the parameters in the sample by comparing the retention times of the peaks in the sample chromatogram with those of the peaks in standard chromatograms. The width of the retention time window used to make identifications should be based upon measurements of ac- tual retention time variations of standards over the course of a day. Three times the standard deviation of a retention time for a compound can be used to calculate a sug- gested window size; however, the experience of the analyst should weigh heavily in the interpretation of chromatograms.

  - If the response for a peak exceeds the working range of the system, dilute the ex- tract and reanalyze.

  - If the measurement of the peak re- sponse is prevented by the presence of inter- ferences, further cleanup is required.

14. Calculations

14.1 Determine the concentration of indi- vidual compounds in the sample.

14.1.1 If the external standard calibration procedure is used, calculate the amount of material injected from the peak response using the calibration curve or calibration factor determined in Section 7.2.2. The con- centration in the sample can be calculated from Equation 2.

#### Pt. 136, App. A, Meth. 610

40 CFR Ch. I (7–1–17 Edition)

Concentration (g/L) 

where:

AVt 

Vi Vs 

Equation   2

REFERENCES

- 40 CFR part 136, appendix B.

- ‘‘Determination of Polynuclear Aro- matic Hydrocarbons in Industrial and Munic- ipal Wastewaters,’’ EPA 600/4–82–025, Na- tional Technical Information Service, PB82–

A = Amount of material injected (ng). Vi = Volume of extract injected (L). Vt = Volume of total extract (L).

Vs = Volume of water extracted (mL).

13.1.2 If the internal standard calibration procedure is used, calculate the concentra- tion in the sample using the response factor (RF) determined in Section 7.3.2 and Equa- tion 3.

As Is 

## Concentration (g/L) 

Ais RFVo 

Equation   3

where:

As  = Response for the parameter to be meas- ured.

Ais = Response for the internal standard.

Is   =  Amount  of  internal  standard  added  to each extract (g).

Vo = Volume of water extracted (L).

14.2 Report results in g/L without correc- tion for recovery data. All QC data obtained should be reported with the sample results.

15. Method Performance

  - The method detection limit (MDL) is defined as the minimum concentration of a substance that can be measured and reported with 99% confidence that the value is above zero. 1 The MDL concentrations listed  in Table 1 were obtained using reagent water. 11 Similar results were achieved using rep- resentative wastewaters. MDL for the GC ap- proach were not determined. The MDL actu- ally achieved in a given analysis will vary depending on instrument sensitivity and ma- trix  effects.

  - This method has been tested for lin- earity of spike recovery from reagent water and has been demonstrated to be applicable over the concentration range from 8 MDL to 800 MDL 11 with the following exception: benzo(ghi)perylene recovery at 80 and 800  MDL were low (35% and 45%, respectively).

  - This method was tested by 16 labora- tories using reagent water, drinking water, surface water, and three industrial wastewaters spiked at six concentrations over the range 0.1 to 425 g/L. 12 Single oper- ator precision, overall precision, and method accuracy were found to be directly related to the concentration of the parameter and es- sentially independent of the sample matrix. Linear equations to describe these relation- ships are presented in Table 4.

258799, Springfield, Virginia 22161, June 1982.

- ASTM Annual Book of Standards, Part 31, D3694–78. ‘‘Standard Practices for Prepa- ration of Sample Containers and for Preser- vation of Organic Constituents,’’ American Society for Testing and Materials, Philadel- phia.

- ‘‘Carcinogens—Working With Carcino- gens,’’ Department of Health, Education, and Welfare, Public Health Service, Center for Disease Control, National Institute for Occu- pational Safety and Health, Publication No. 77–206, August 1977.

- ‘‘OSHA Safety and Health Standards, General Industry,’’ (29 CFR part 1910), Occu- pational Safety and Health Administration, OSHA 2206 (Revised, January 1976).

- ‘‘Safety in Academic Chemistry Labora- tories,’’ American Chemical Society Publica- tion, Committee on Chemical Safety, 3rd Edition, 1979.

- Provost,  L.P.,  and  Elder,  R.S.  ‘‘Interpre- tation   of   Percent   Recovery   Data,’’   American Laboratory, 15, 58–63  (1983).  (The  value  2.44 used  in  the  equation  in  Section  8.3.3  is  two times the value 1.22 derived in this report.)

- ASTM Annual Book of Standards, Part 31, D3370–76. ‘‘Standard Practices for Sam- pling Water,’’ American Society for Testing and  Materials,  Philadelphia.

- ‘‘Methods 330.4 (Titrimetric, DPD-FAS) and 330.5 (Spectrophotometric, DPD) for Chlorine, Total Residual,’’ Methods for Chemical Analysis of Water and Wastes, EPA–600/4–79–020, U.S. Environmental Pro- tection Agency, Environmental Monitoring and Support Laboratory, Cincinnati, Ohio 45268, March 1979.

- Burke, J.A. ‘‘Gas Chromatography for Pesticide Residue Analysis; Some Practical Aspects,’’ Journal of the Association of Official Analytical Chemists, 48, 1037 (1965).

- Cole, T., Riggin, R., and Glaser, J. ‘‘Evaluation of Method Detection Limits and Analytical Curve for EPA Method 610— PNAs,’’ International Symposium on Polynuclear Aromatic Hydrocarbons, 5th, Battelle’s Columbus Laboratories, Colum- bus, Ohio (1980).

- ‘‘EPA Method Study 20, Method 610 (PNA’s),’’ EPA 600/4–84–063, National Tech- nical Information Service, PB84–211614, Springfield, Virginia 22161, June 1984.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 610

TABLE 1—HIGH PERFORMANCE LIQUID CHROMATOGRAPHY CONDITIONS AND METHOD DETECTION LIMITS

| Parameter | Retention time (min) | Column capacity factor (k) | Method detection limit (g/ L) a |
| --- | --- | --- | --- |
| Naphthalene ............................................................................................................................ | 16.6 | 12.2 | 1.8 |
| Acenaphthylene ....................................................................................................................... | 18.5 | 13.7 | 2.3 |
| Acenaphthene ......................................................................................................................... | 20.5 | 15.2 | 1.8 |
| Fluorene .................................................................................................................................. | 21.2 | 15.8 | 0.21 |
| Phenanthrene .......................................................................................................................... | 22.1 | 16.6 | 0.64 |
| Anthracene .............................................................................................................................. | 23.4 | 17.6 | 0.66 |
| Fluoranthene ........................................................................................................................... | 24.5 | 18.5 | 0.21 |
| Pyrene ..................................................................................................................................... | 25.4 | 19.1 | 0.27 |
| Benzo(a)anthracene ................................................................................................................ | 28.5 | 21.6 | 0.013 |
| Chrysene ................................................................................................................................. | 29.3 | 22.2 | 0.15 |
| Benzo(b)fluoranthene .............................................................................................................. | 31.6 | 24.0 | 0.018 |
| Benzo(k)fluoranthene .............................................................................................................. | 32.9 | 25.1 | 0.017 |
| Benzo(a)pyrene ....................................................................................................................... | 33.9 | 25.9 | 0.023 |
| Dibenzo(a,h)anthracene .......................................................................................................... | 35.7 | 27.4 | 0.030 |
| Benzo(ghi)perylene ................................................................................................................. | 36.3 | 27.8 | 0.076 |
| Indeno(1,2,3-cd)pyrene ........................................................................................................... | 37.4 | 28.7 | 0.043 |

HPLC column conditions: Reverse phase HC-ODS Sil-X, 5 micron particle size, in a 25 cm 2.6 mm ID stainless steel col- umn. Isocratic elution for 5 min. using acetonitrile/water (4 + 6), then linear gradient elution to 100% acetonitrile over 25 min. at

0.5 mL/min flow rate. If columns having other internal diameters are used, the flow rate should be adjusted to maintain a linear velocity of 2 mm/sec.

a The MDL for naphthalene, acenaphthylene, acenaphthene, and fluorene were determined using a UV detector. All others were determined using a fluorescence detector.

TABLE 2—GAS CHROMATOGRAPHIC CONDITIONS AND RETENTION TIMES

TABLE 2—GAS CHROMATOGRAPHIC CONDITIONS AND RETENTION TIMES—Continued

| Parameter | Retention time (min) |
| --- | --- |
| Benzo(k)fluoranthene .......................................... | 28.0 |
| Benzo(a)pyrene ................................................... | 29.4 |
| Dibenzo(a,h)anthracene ...................................... | 36.2 |
| Indeno(1,2,3-cd)pyrene ....................................... | 36.2 |
| Benzo(ghi)perylene .............................................. | 38.6 |

Parameter

Retention time (min)

Naphthalene  ........................................................	4.5

Acenaphthylene ...................................................	10.4

Acenaphthene ......................................................	10.8

Fluorene ...............................................................	12.6

Phenanthrene ......................................................	15.9

Anthracene  ..........................................................	15.9

Fluoranthene ........................................................	19.8

Pyrene  .................................................................	20.6

Benzo(a)anthracene ............................................	24.7

Chrysene  .............................................................	24.7

Benzo(b)fluoranthene ..........................................	28.0

GC Column conditions: Chromosorb W-AW-DCMS (100/120 mesh) coated with 3% OV–17 packed in a 1.8 2 mm ID glass column with nitrogen carrier gas at 40 mL/min. flow rate. Column temperature was held at 100 C for 4 min., then pro- grammed at 8 C/min. to a final hold at 280 C.

TABLE 3—QC ACCEPTANCE CRITERIA—METHOD 610

| Parameter | Test conc. (g/L) | Limit for s (g/L) | Range for X¯ (g/L) | Range for P, Ps (%) |
| --- | --- | --- | --- | --- |
| Acenaphthene ....................................................................................... | 100 | 40.3 | D–105.7 | D–124 |
| Acenaphthylene ..................................................................................... | 100 | 45.1 | 22.1–112.1 | D–139 |
| Anthracene ............................................................................................ | 100 | 28.7 | 11.2–112.3 | D–126 |
| Benzo(a)anthracene .............................................................................. | 10 | 4.0 | 3.1–11.6 | 12–135 |
| Benzo(a)pyrene ..................................................................................... | 10 | 4.0 | 0.2–11.0 | D–128 |
| Benzo(b)fluor-anthene ........................................................................... | 10 | 3.1 | 1.8–13.8 | 6–150 |
| Benzo(ghi)perylene ............................................................................... | 10 | 2.3 | D–10.7 | D–116 |
| Benzo(k)fluo-ranthene ........................................................................... | 5 | 2.5 | D–7.0 | D–159 |
| Chrysene ............................................................................................... | 10 | 4.2 | D–17.5 | D–199 |
| Dibenzo(a,h)an-thracene ....................................................................... | 10 | 2.0 | 0.3–10.0 | D–110 |
| Fluoranthene ......................................................................................... | 10 | 3.0 | 2.7–11.1 | 14–123 |
| Fluorene ................................................................................................ | 100 | 43.0 | D–119 | D–142 |
| Indeno(1,2,3–cd)pyrene ........................................................................ | 10 | 3.0 | 1.2–10.0 | D–116 |
| Naphthalene .......................................................................................... | 100 | 40.7 | 21.5–100.0 | D–122 |
| Phenanthrene ........................................................................................ | 100 | 37.7 | 8.4–133.7 | D–155 |
| Pyrene ................................................................................................... | 10 | 3.4 | 1.4–12.1 | D–140 |

s = Standard deviation of four recovery measurements, in g/L (Section 8.2.4). X¯ = Average recovery for four recovery measurements, in g/L (Section 8.2.4).

P, Ps  = Percent recovery measured (Section 8.3.2, Section 8.4.2). D = Detected; result must be greater than zero.

NOTE: These criteria are based directly upon the method performance data in Table 4. Where necessary, the limits for recov- ery have been broadened to assure applicability of the limits to concentrations below those used to develop Table 4.

#### Pt. 136, App. A, Meth. 610

40 CFR Ch. I (7–1–17 Edition)

TABLE 4—METHOD ACCURACY AND PRECISION AS FUNCTIONS OF CONCENTRATION—METHOD 610

| Parameter | Accuracy, as recovery, X (g/L) | Single analyst precision, sr (g/L) | Overall preci- sion, S (g/L) |
| --- | --- | --- | --- |
| Acenaphthene ................................................................................................... | 0.52C + 0.54 | 0.39X¯ + 0.76 | 0.53X¯ + 1.32 |
| Acenaphthylene ................................................................................................. | 0.69C ¥ 1.89 | 0.36X¯ + 0.29 | 0.42X¯ + 0.52 |
| Anthracene ........................................................................................................ | 0.63C ¥ 1.26 | 0.23X¯ + 1.16 | 0.41X¯ + 0.45 |
| Benzo(a)anthracene .......................................................................................... | 0.73C + 0.05 | 0.28X¯ + 0.04 | 0.34X¯ + 0.02 |
| Benzo(a)pyrene ................................................................................................. | 0.56C + 0.01 | 0.38X¯ ¥ 0.01 | 0.53X¯ ¥ 0.01 |
| Benzo(b)fluoranthene ........................................................................................ | 0.78C + 0.01 | 0.21X¯ + 0.01 | 0.38X¯ ¥ 0.00 |
| Benzo(ghi)perylene ........................................................................................... | 0.44C + 0.30 | 0.25X¯ + 0.04 | 0.58X¯ + 0.10 |
| Benzo(k)fluoranthene ........................................................................................ | 0.59C + 0.00 | 0.44X¯ ¥ 0.00 | 0.69X¯ + 0.01 |
| Chrysene ........................................................................................................... | 0.77C ¥ 0.18 | 0.32X¯ ¥ 0.18 | 0.66X¯ ¥ 0.22 |
| Dibenzo(a,h)anthracene .................................................................................... | 0.41C + 0.11 | 0.24X¯ + 0.02 | 0.45X¯ + 0.03 |
| Fluoranthene ..................................................................................................... | 0.68C + 0.07 | 0.22X¯ + 0.06 | 0.32X¯ + 0.03 |
| Fluorene ............................................................................................................ | 0.56C ¥ 0.52 | 0.44X¯ ¥ 1.12 | 0.63X¯ ¥ 0.65 |
| Indeno(1,2,3–cd)pyrene .................................................................................... | 0.54C + 0.06 | 0.29X¯ + 0.02 | 0.42X¯ + 0.01 |
| Naphthalene ...................................................................................................... | 0.57C ¥ 0.70 | 0.39X¯ ¥ 0.18 | 0.41X¯ + 0.74 |
| Phenanthrene .................................................................................................... | 0.72C ¥ 0.95 | 0.29X¯ + 0.05 | 0.47X¯ ¥ 0.25 |
| Pyrene ............................................................................................................... | 0.69C ¥ 0.12 | 0.25X¯ + 0.14 | 0.42X¯ ¥ 0.00 |

X= Expected recovery for one or more measurements of a sample containing a concentration of C, in g/L.

sr= Expected single analyst standard deviation of measurements at an average concentration found of X¯ , in g/L. S= Expected interlaboratory standard deviation of measurements at an average concentration found of X¯ , in g/L. C = True value for the concentration, in g/L.

X¯ = Average recovery found for measurements of samples containing a concentration of C, in g/L.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 610

Pt. 136, App. A, Meth. 611

40 CFR Ch. I (7–1–17 Edition)

METHOD  611—HALOETHERS

- Scope and Application

  - This method covers the determination of certain haloethers. The following param- eters can be determined by this method:

| Parameter | STORET No. | CAS No. |
| --- | --- | --- |
| Bis(2-chloroethyl) ether ............. | 34273 | 111–44–4 |
| Bis(2-chloroethoxy) methane .... | 34278 | 111–91–1 |
| Bis(2-chloroisopropyl) ether ...... | 34283 | 108–60–1 |
| 4-Bromophenyl phenyl ether ..... | 34636 | 101–55–3 |
| 4-Chlorophenyl phenyl either .... | 34641 | 7005–72–3 |

  - This is a gas chromatographic (GC) method applicable to the determination of the compounds listed above in municipal and industrial discharges as provided under 40 CFR 136.1. When this method is used to ana- lyze unfamiliar samples for any or all of the compounds above, compound identifications should be supported by at least one addi- tional qualitative technique. This method describes  analytical  conditions  for  a  second

gas chromatographic column that  can  be used to confirm measurements made with the primary column. Method 625 provides gas chromatograph/mass spectrometer (GC/MS) conditions appropriate for  the  qualitative and quantitative confirmation of results  for all of the parameters listed above, using the extract produced by this method.

  - The method detection limit (MDL, de- fined in Section 14.1) 1 for each parameter is listed in Table 1. The MDL for a specific wastewater may differ from those listed, de- pending upon the nature of interferences  in the sample matrix.

  - The sample extraction and concentra- tion steps in this method are essentially the same as in Methods 606, 608, 609, and 612. Thus, a single sample may be extracted to measure the parameters included in the scope of each of these methods. When clean- up is required, the concentration levels must be high  enough  to  permit  selecting  aliquots, as necessary, to apply appropriate cleanup procedures. The analyst is allowed the lati- tude,      under      Section      12,      to      select

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 611

chromatographic conditions appropriate for the simultaneous measurement of combina- tions of these parameters.

  - Any modification of this method,  be- yond those expressly permitted, shall be con- sidered as a major modification subject to application and approval of alternate test procedures under 40 CFR 136.4 and 136.5.

  - This method is restricted to use by or under the supervision of analysts experi- enced in the use of a gas chromatograph and in the interpretation of gas chromatograms. Each analyst must demonstrate  the  ability to generate acceptable results with this method using the procedure described in Sec- tion 8.2.

- Summary of Method

  - A measured volume of sample, ap- proximately 1–L, is extracted with  meth- ylene chloride using a separatory funnel. The methylene chloride extract is dried and ex- changed to hexane during concentration to a volume of 10 mL or less. The extract is sepa- rated by gas chromatography and the param- eters are then measured with a halide spe- cific  detector. 2

  - The method provides a Florisil column cleanup procedure to aid  in  the  elimination of interferences that may be encountered.

- Interferences

  - Method interferences may be caused by contaminants in solvents, reagents, glass- ware, and other sample processing hardware that lead to discrete artifacts and/or ele- vated baselines in gas chromatograms. All of these materials must be routinely dem- onstrated to be free from interferences under the conditions of the analysis by running laboratory reagent blanks as described in Section 8.1.3.

    - Glassware must be scrupulously cleaned. 3 Clean all glassware as soon as pos- sible after use by rinsing with the last sol- vent used in it. Solvent rinsing should be fol- lowed be detergent washing with hot water, and rinses with tap water and distilled water. The glassware should then be drained dry, and heated in a muffle furnace at 400 C for 15 to 30 min. Some thermally stable ma- terials, such a PCBs, may not be eliminated by this treatment. Solvent rinses with ace- tone and pesticide quality hexane may be substituted for the muffle furnace heating. Thorough rinsing with such solvents usually eliminates PCB interference. Volumetric ware should not be heated in a muffle fur- nace. After drying and cooling, glassware should be sealed and stored in a clean envi- ronment to prevent any accumulation of dust or other contaminants. Store inverted or capped with aluminum foil.

    - The use of high purity reagents and solvents helps to minimize interference prob-

lems. Purification of solvents by distillation in all-glass systems may be required.

  - Matrix interferences may be caused by contaminants that are co-extracted from the sample. The extent of matrix interferences will vary considerably from source to source, depending upon the nature and diversity  of the industrial complex or municipality being sampled.  The  cleanup  procedure  in  Section

11 can be used to overcome many of these interferences, but unique samples may re- quire additional cleanup approaches to achieve the MDL listed in Table 1.

  - Dichlorobenzenes are known to coelute with  haloethers under  some gas chromatographic conditions. If these mate- rials are present together in a sample, it may be necessary to analyze the extract with two different column packings to com- pletely resolve all of the compounds.

- Safety

4.1   The   toxicity   or   carcinogenicity   of each  reagent  used  in  this  method  has  not been precisely defined; however, each chem- ical compound should be treated as a poten- tial health hazard. From this viewpoint, ex- posure to these chemicals must be reduced to the lowest possible level by whatever means available. The laboratory is responsible for maintaining   a   current   awareness   file   of OSHA  regulations  regarding  the  safe  han- dling of the chemicals specified in this meth- od. A reference file of material data handling sheets should also be made available to all personnel involved in the chemical analysis. Additional  references  to  laboratory  safety are available and have been identified 4M6 for the information of the analyst.

- Apparatus and Materials

  - Sampling equipment, for discrete or composite  sampling.

    - Grab sample bottle—1-L or 1-qt, amber glass, fitted with a screw cap lined with Teflon. Foil may be substituted for Tef- lon if the sample is not corrosive. If amber bottles are not available, protect samples from light. The bottle and cap liner must be washed, rinsed with acetone or methylene chloride, and dried before use to minimize contamination.

    - Automatic sampler (optional)—The sampler must incorporate glass sample con- tainers for the collection of a minimum of 250 mL of sample. Sample containers must be kept refrigerated at 4 C and protected from light during compositing. If the sampler uses a peristaltic pump, a minimum length of compressible silicone rubber tubing may be used. Before use, however, the compressible tubing should be thoroughly rinsed with methanol, followed by repeated rinsings with distilled water to minimize the potential for contamination  of  the  sample.  An  integrating

#### Pt. 136, App. A, Meth. 611

flow meter is required to collect flow propor- tional  composites.

  - Glassware (All specifications are sug- gested. Catalog numbers are included for il- lustration only.):

    - Separatory funnel—2-L, with Teflon stopcock.

    - Drying column—Chromatographic column, approximately 400 mm long 19 mm ID,  with  coarse  frit  filter  disc.

    - Chromatographic column—400 mm long 19 mm ID, with Teflon stopcock and coarse frit filter disc at bottom (Kontes K– 420540–0224 or equivalent).

    - Concentrator tube, Kuderna-Dan- ish—10-mL, graduated (Kontes K–570050–1025 or equivalent). Calibration must  be  checked at the volumes employed in the test. Ground glass stopper is used to prevent evaporation of  extracts.

    - Evaporative flask, Kuderna-Danish— 500-mL (Kontes K–570001–0500 or equivalent). Attach  to  concentrator  tube  with  springs.

    - Snyder column, Kuderna-Danish— Three-ball macro (Kontes K–503000–0121 or equivalent).

    - Vials—10 to 15-mL, amber glass, with Teflon-lined screw cap.

  - Boiling chips—Approximately 10/40 mesh. Heat to 400 C for 30 min or Soxhlet ex- tract  with  methylene  chloride.

  - Water bath—Heated, with concentric ring cover, capable of temperature control (2 C). The bath should be used in a hood.

  - Balance—Analytical, capable of accu- rately weighing 0.0001 g.

  - Gas chromatograph—An analytical system complete with temperature program- mable gas chromatograph suitable for on- column injection and all required accessories including  syringes,  analytical   columns, gases, detector, and strip-chart recorder. A data system is recommended for measuring peak areas.

    - Column 1—1.8 m long 2 mm ID glass, packed with 3% SP–1000 on Supelcoport (100/120 mesh) or equivalent. This column was used to develop the method performance statements in Section 14. Guidelines for the use of alternate column packings are provided in Section 12.1.

    - Column 2—1.8 m long  2  mm  ID glass, packed with 2,6-diphenylene  oxide polymer  (60/80  mesh),  Tenax,  or  equivalent.

    - Detector—Halide specific detector: electrolytic	conductivity	or microcoulometric. These detectors have proven effective in the analysis of wastewaters for the parameters listed in the scope (Section 1.1). The Hall conductivity de- tector was used to develop the method per- formance statements in Section 14. Guide- lines for the use of alternate detectors are provided in Section 12.1. Although less selec- tive, an electron capture detector is an ac- ceptable alternative.

#### 40 CFR Ch. I (7–1–17 Edition)

- Reagents

  - Reagent water—Reagent water is de- fined as a water in which  an  interferent  is not observed at the  MDL  of  the  parameters of  interest.

  - Sodium thiosulfate—(ACS) Granular.

  - Acetone, hexane, methanol, methylene chloride, petroleum ether (boiling range 30– 60 C)—Pesticide quality or equivalent.

  - Sodium sulfate—(ACS) Granular, an- hydrous. Purify by heating at 400 C for 4 h in a shallow tray.

  - Florisil—PR Grade (60/100 mesh). Pur- chase activated at 1250 F and store in the dark in glass containers with ground glass stoppers or foil-lined screw caps. Before use, activate each batch at least 16 h at 130 C in a foil-covered glass container and allow to cool.

  - Ethyl ether—Nanograde, redistilled in glass if necessary.

    - Ethyl ether must be shown to be free of peroxides before it is used as indicated by EM Laboratories Quant  test  strips.  (Avail- able from Scientific Products Co., Cat. No. P1126–8, and other suppliers.)

    - Procedures recommended for re- moval of peroxides are provided with the test strips. After cleanup, 20 mL of ethyl alcohol preservative must be added to each liter of ether.

  - Stock standard solutions (1.00 g/L)—

Stock standard solutions can be prepared from pure standard materials or purchased as certified solutions.

    - Prepare stock standard solutions by accurately weighing about 0.0100 g of pure material. Dissolve  the  material  in  acetone and dilute to volume in a 10-mL volumetric flask. Larger volumes can be used at the con- venience of the analyst. When compound pu- rity is assayed to be  96%  or  greater,  the weight can be used without correction to cal- culate the concentration of the stock stand- ard. Commercially  prepared  stock  standards can be used at any concentration if they are certified by the manufacturer or by an inde- pendent  source.

    - Transfer the stock standard solu- tions into Teflon-sealed screw-cap bottles. Store at 4 C and protect from light. Stock standard solutions should be checked fre- quently for signs of degradation or evapo- ration, especially just prior to preparing calibration standards from them.

    - Stock standard solutions must be re- placed after six months, or sooner if com- parison with check standards indicates a problem.

6.8 Quality control check sample con- centrate—See Section 8.2.1.

- Calibration

  - Establish gas chromatographic oper- ating conditions equivalent to those given in Table  1.  The  gas  chromatographic  system

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 611

can be calibrated using the external standard technique (Section 7.2) or the internal stand- ard technique (Section 7.3).

where:

Equation   1

  - External standard calibration proce- dure:

    - Prepare calibration standards at a minimum of three concentration levels  for each parameter of interest by adding vol- umes of one or more stock standards to a volumetric flask and diluting to volume with hexane. One of the external standards should be at a concentration near, but above, the MDL (Table 1) and the other concentrations should correspond to the expected range of concentrations found in real samples or should define the working range of the detec- tor.

    - Using injections of 2 to 5 L, analyze

each calibration standard according to Sec- tion 12 and tabulate peak height or area re- sponses against  the mass injected. The re- sults can be used to prepare a calibration curve for each compound. Alternatively, if the ratio of response to amount injected (calibration factor) is a constant over the working range (<10% relative standard devi- ation, RSD), linearity through the origin can be assumed and the average ratio or calibra- tion factor can be used in place of a calibra- tion curve.

  - Internal standard calibration proce- dure—To use this approach, the analyst must select one or more internal standards that are similar in analytical behavior to the compounds of interest. The analyst must fur- ther demonstrate that the measurement of the internal standard is not affected by method or matrix interferences. Because of these limitations, no internal standard  can be suggested that is applicable to all sam- ples.

    - Prepare calibration standards at a minimum of three concentration levels  for each parameter of interest by adding vol- umes of one or more stock standards to a volumetric flask. To each calibration stand- ard, add a known constant amount of one or more internal standards, and dilute to vol- ume with hexane. One of the standards should be at a concentration near, but above, the MDL and the other concentrations should correspond to the expected range of concentrations found in real samples or should define the working range of the detec- tor.

    - Using injections of 2 to 5 L, analyze

each calibration standard according to Sec- tion 12 and tabulate peak height or area re- sponses against concentration for each com- pound and internal standard. Calculate re- sponse factors (RF) for each compound using Equation 1.

As Cis 

## RF 

Ais Cs 

As  = Response for the parameter to be meas-

ured.

Ais = Response for the internal standard.

Cis  = Concentration of the internal standard (g/L).

Cs   =  Concentration  of  the  parameter  to  be measured (g/L).

If the RF value over the working range is a constant (<10% RSD), the RF can be assumed to be invariant and the average RF can be used for calculations. Alternatively, the re- sults can be used to plot a calibration curve of response ratios, As/Ais, vs. RF.

  - The working calibration curve, cali- bration factor, or RF must be verified on each working day by the measurement of one or more calibration standards. If the re- sponse for any parameter varies from the predicted response by more than 15%, a new calibration curve must be prepared for that compound.

  - The cleanup procedure in Section 11 utilizes Florisil column chromatography. Florisil from different  batches  or  sources may vary in adsorptive capacity. To stand- ardize the amount of Florisil which  is  used, the use of lauric acid value 7 is  suggested. The referenced procedure determines the ad- sorption from hexane solution of lauric  acid (mg) per g of Florisil. The amount of Florisil to be  used  for each  column  is  calculated by dividing 110 by this ratio and multiplying by 20 g.

  - Before using any cleanup procedure, the analyst must process a series of calibra- tion standards through the procedure to vali- date elution patterns and the absence of interferences from the reagents.

- Quality Control

  - Each laboratory that uses this method is required to operate a formal quality  con- trol program. The minimum requirements of this program consist of an initial demonstra- tion of laboratory capability and an ongoing analysis of spiked samples to evaluate and document data quality. The laboratory must maintain records to document the quality of data that is generated. Ongoing data quality checks are compared with established per- formance criteria to determine if the results of analyses meet the performance character- istics of the method. When results of sample spikes indicate atypical method perform- ance, a quality control check  standard  must be analyzed to confirm that the measure- ments were performed in an in-control mode of operation.

    - The analyst must make an initial, one-time, demonstration of the ability to generate acceptable accuracy and precision with this method. This  ability  is  established as described in Section 8.2.

#### Pt. 136, App. A, Meth. 611

    - In recognition of advances that are occurring in chromatography, the analyst is permitted certain options (detailed in Sec- tions 10.4, 11.1, and 12.1) to improve the sepa- rations or lower the cost of measurements. Each time such a modification is  made  to the method, the analyst is required to repeat the procedure in Section 8.2.

    - Before processing any samples, the analyst must analyze a  reagent  water  blank to demonstrate that interferences from the analytical system and glassware are under control. Each time a set of samples is ex- tracted or reagents are changed, a reagent water blank must be processed as a safe- guard  against  laboratory  contamination.

    - The laboratory must, on an ongoing basis, spike and analyze a minimum of 10% of all samples to monitor and evaluate lab- oratory data quality. This procedure is de- scribed in Section 8.3.

    - The laboratory must, on an ongoing basis, demonstrate through the analyses of quality control  check standards  that  the op- eration of the measurement system is in con- trol.  This  procedure  is  described  in  Section

8.4. The frequency of the check standard analyses is equivalent to 10% of all samples analyzed but may be reduced if spike recov- eries from samples (Section 8.3) meet all specified quality control criteria.

    - The laboratory must maintain per- formance records to document the quality of data that is generated. This procedure is de- scribed in Section 8.5.

  - To establish the ability to generate acceptable accuracy and precision, the ana- lyst must perform the following operations.

    - A quality control (QC) check sample concentrate is required containing each pa- rameter of interest at a concentration of 100

g/mL in acetone. The QC check sample con- centrate must be obtained from the U.S. En- vironmental Protection Agency, Environ- mental Monitoring and Support Laboratory in Cincinnati, Ohio, if available. If not avail- able from that source, the QC check sample concentrate must be obtained from another external source. If not available from either source above, the QC check sample con- centrate must be prepared by the laboratory using stock standards prepared independ- ently from those used for calibration.

    - Using a pipet, prepare QC check sam- ples at a concentration of 100 g/L by adding

1.00 mL of QC check sample concentrate to each of four 1–L aliquots of reagent water.

    - Analyze the well-mixed QC check samples according to the  method  beginning in Section 10.

    - Calculate the average recovery (X¯ ) in

g/L, and the standard deviation of the re- covery (s) in g/L, for each parameter using the four results.

    - For each parameter compare s and X¯

with the corresponding acceptance criteria for   precision   and   accuracy,   respectively,

#### 40 CFR Ch. I (7–1–17 Edition)

found in Table 2. If s and X¯ for all param- eters of interest meet the acceptance cri- teria, the system performance is acceptable and analysis of actual samples can begin. If any individual s exceeds the precision limit

or any individual X¯  falls outside the range

for accuracy, the system performance is un- acceptable for that parameter. Locate and correct the source of the problem and repeat the test for all parameters of interest begin- ning with Section 8.2.2.

  - The laboratory must, on an ongoing basis, spike at least 10% of the samples from each sample site being monitored to assess accuracy. For laboratories analyzing one to ten samples per month, at least one spiked sample per month is required.

    - The concentration of the spike in the sample should be determined as follows:

      - If, as in compliance monitoring, the concentration of a specific parameter in the sample is being checked against a regu- latory concentration limit, the spike should be at that limit or 1 to 5 times higher than the background concentration determined in Section 8.3.2, whichever concentration would be larger.

      - If the concentration of a specific parameter in the sample  is  not  being checked against a limit specific to that pa- rameter, the spike should be at 100 g/L or 1 to 5  times  higher than  the  background  con- centration determined in Section 8.3.2, whichever concentration would be larger.

      - If it is impractical to determine background levels before spiking (e.g., max- imum holding times will be exceeded), the spike concentration should be (1) the regu- latory concentration limit, if any; or, if none

(2) the larger of either 5  times  higher  than the expected background  concentration  or 100 g/L.

    - Analyze one sample aliquot to deter- mine the background concentration (B) of each parameter. If necessary, prepare a new QC check sample concentrate (Section 8.2.1) appropriate for the background concentra- tions in the sample. Spike a second sample aliquot with 1.0 mL of the QC check sample concentrate and analyze it to determine the concentration after spiking (A) of each pa- rameter. Calculate each percent recovery (P) as 100(A¥B)%/T, where T is the known true value of the spike.

    - Compare the percent recovery (P) for each parameter with the corresponding QC acceptance criteria found in Table 2. These acceptance criteria were calculated to in- clude an allowance for error in measurement of both the background and spike concentra- tions, assuming a spike  to  background  ratio of 5:1. This error will be accounted for to the extent that the analyst’s spike to back- ground ratio approaches 5:1. 8 If spiking was performed at a concentration lower than 100

g/L, the analyst must use either the QC ac- ceptance  criteria  in  Table  2,  or  optional  QC

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 611

acceptance criteria calculated for the spe- cific spike concentration. To calculate op- tional acceptance criteria for the recovery of a parameter: (1) Calculate accuracy (X) using the equation in Table 3, substituting the spike concentration (T) for C; (2) cal- culate overall precision (S) using the equa-

tion in Table 3, substituting Xfor X¯ ; (3) cal-

culate the range for recovery at the spike concentration as (100 X/T)2.44(100 S/T)%. 8

    - If any individual P falls outside the designated range for recovery, that param- eter has failed the acceptance criteria. A check standard containing each parameter that failed the criteria must be analyzed as described in Section 8.4.

  - If any parameter fails the acceptance criteria for recovery in Section 8.3, a QC check standard containing each parameter that failed must be prepared and analyzed.

NOTE: The frequency for the required anal- ysis of a QC check standard will depend upon the number of parameters being simulta- neously tested, the complexity of the sample matrix, and the performance of the labora- tory.

    - Prepare the QC check standard by adding 1.0 m/L of QC check sample con- centrate (Section 8.2.1 or 8.3.2) to 1 L of rea- gent water.  The  QC  check  standard  needs only to contain the parameters that failed criteria  in  the  test  in  Section  8.3.

    - Analyze the QC check standard to determine the concentration measured (A) of each parameter. Calculate each percent re- covery (Ps) as 100 (A/T)%, where T is the true value of the standard concentration.

    - Compare the percent recovery (Ps) for each parameter with the corresponding QC acceptance criteria found in Table 2. Only parameters that failed the test in Section 8.3 need to be compared with these  criteria.  If the recovery of any such parameter falls out- side the designated range, the laboratory performance for that parameter is judged to be out of control, and the problem must be immediately identified and corrected. The analytical result for that parameter in the unspiked sample is suspect  and may not  be reported for regulatory compliance purposes.

  - As part of the QC program for the lab- oratory, method accuracy for wastewater samples must be assessed and records must be  maintained.  After  the  analysis  of  five

spiked wastewater samples as in Section 8.3, calculate  the  average  percent  recovery  (P¯ )

and the standard deviation of the percent re- covery (sp). Express the accuracy assessment

as a percent recovery interval from P¯ –2sp to P¯ + 2sp. If P¯ = 90% and sp = 10%, for example,

the accuracy interval is expressed as 70– 110%. Update the accuracy  assessment  for each parameter on a regular basis (e.g. after each five to  ten  new  accuracy  measure- ments).

  - It is recommended that the laboratory adopt additional quality assurance practices

for use  with  this method.  The  specific  prac- tices that  are  most  productive  depend  upon the needs of the laboratory and the nature of the samples. Field duplicates may be ana- lyzed to assess the precision of the environ- mental measurements. When doubt exists over the identification of a peak on the chro- matogram, confirmatory techniques such as gas chromatography with a dissimilar col- umn, specific element detector, or mass spectrometer must be used. Whenever pos- sible, the laboratory should analyze standard reference materials and participate in rel- evant performance evaluation studies.

- Sample Collection, Preservation, and Handling

  - Grab samples must be collected  in glass containers. Conventional sampling practices 9 should be followed, except  that the bottle must not be prerinsed with sample before collection. Composite samples should be collected in refrigerated  glass  containers in accordance with the requirements of the program. Automatic sampling equipment must be as free as possible of Tygon tubing and other potential sources of contamina- tion.

  - All samples must be iced or refrig- erated at 4 C from the time of collection until extraction. Fill the sample bottles and, if residual chlorine is present, add 80 mg of sodium thiosulfate per liter of sample and mix well. EPA Methods 330.4 and 330.5 may be used for measurement of residual chlo- rine. 10 Field test kits are available for this purpose.

  - All samples must be extracted within 7 days of collection and completely analyzed within 40 days of extraction. 2

- Sample Extraction

  - Mark the water meniscus on the side of the sample bottle for later determination of sample volume. Pour the entire sample into a 2-L separatory funnel.

  - Add 60 mL methylene chloride to the sample bottle, seal, and shake 30  s  to  rinse the inner surface. Transfer the solvent to the separatory funnel and extract the sample by shaking the funnel for 2 min with periodic venting to release excess pressure. Allow the organic layer to separate from  the  water phase for a minimum of 10 min. If the emul- sion interface between layers is more than one-third the volume of the solvent  layer, the analyst must employ mechanical tech- niques to complete the phase separation. The optimum technique depends upon the sam- ple,  but  may  include  stirring,  filtration   of the emulsion through glass wool, centrifuga- tion, or other physical methods. Collect the methylene chloride extract in a 250-mL Er- lenmeyer  flask.

#### Pt. 136, App. A, Meth. 611

  - Add a second 60-mL volume of meth- ylene chloride to the sample bottle and re- peat the extraction procedure a second time, combining the extracts in the Erlenmeyer flask. Perform a third extraction in the same manner.

  - Assemble a Kuderna-Danish (K-D) concentrator by attaching a 10-mL concen- trator tube to a 500-mL evaporative flask. Other concentration devices or  techniques may be used in place of the K-D concentrator if the requirements of Section 8.2 are met.

  - Pour the combined extract through a solvent-rinsed drying column containing about 10 cm of anhydrous sodium sulfate, and collect the extract in the K-D concen- trator. Rinse the Erlenmeyer flask and col- umn with 20 to 30 mL of methylene chloride to complete the quantitative transfer.

  - Add one or two clean boiling chips to the evaporative flask and attach a three-ball Snyder column. Prewet the Snyder  column by adding about 1 mL of methylene chloride to the top. Place the K-D apparatus on a hot water bath (60 to 65 C) so that the concen- trator tube is partially immersed in the hot water, and the entire lower rounded surface of the flask is bathed with hot vapor. Adjust the vertical position of the apparatus  and the water temperature as required to com- plete the concentration in 15 to  20  min.  At the proper rate of distillation the balls of the column will actively chatter but the cham- bers will not flood with condensed solvent. When the apparent volume of liquid reaches 1 mL, remove the K-D apparatus and allow it to drain and cool for at least 10 min.

NOTE: Some of the haloethers are very volatile and significant losses will occur in concentration steps if  care  is  not  exercised. It  is  important  to  maintain  a   constant gentle evaporation rate and not to allow the liquid volume to fall below 1 to 2 mL before removing the K-D apparatus from the hot water bath.

  - Momentarily remove the Snyder col- umn, add 50 mL of hexane and a new boiling chip, and reattach the Snyder column.  Raise the temperature of the water bath to 85 to 90

C. Concentrate the  extract  as  in  Section 10.6, except use hexane to prewet the column. The elapsed  time  of  concentration  should  be 5 to 10 min.

  - Remove the Snyder column and rinse the flask and its lower joint into the concen- trator tube with 1 to 2 mL of hexane. A 5-mL syringe is recommended for this operation. Stopper the concentrator tube and store re- frigerated if further processing will not be performed immediately. If the extract  will be stored longer than two days, it should be transferred to a Teflon-sealed screw-cap vial. If the sample extract requires no further cleanup, proceed with gas chromatographic analysis (Section 12). If the sample requires further cleanup, proceed to Section 11.

#### 40 CFR Ch. I (7–1–17 Edition)

  - Determine the original sample vol- ume by refilling the sample bottle to the mark and transferring the liquid to  a  1000- mL graduated cylinder. Record the sample volume to the nearest 5 mL.

- Cleanup and Separation

  - Cleanup procedures may not be nec- essary for a relatively clean sample matrix. If particular circumstances demand the use of a cleanup procedure, the analyst may use the procedure below or any other appropriate procedure. However, the analyst first must demonstrate that the requirements of Sec- tion 8.2 can be met using the method as re- vised to incorporate the cleanup procedure.

  - Florisil column cleanup for haloethers:

    - Adjust  the  sample  extract   volume to 10 mL.

    - Place a weight of Florisil  (nomi- nally 20 g) predetermined by calibration (Section 7.5), into a chromatographic  col- umn. Tap the column to settle the  Florisil and add 1 to 2 cm of anhydrous sodium sul- fate to the top.

    - Preelute the column with 50 to 60 mL of petroleum ether. Discard the eluate and just prior to exposure of the sodium sul- fate layer to the air, quantitatively  transfer the sample extract onto the column by de- cantation and subsequent petroleum ether washings. Discard the eluate. Just prior to exposure of the sodium sulfate layer  to  the air, begin eluting the column with 300 mL of ethyl ether/petroleum  ether (6  + 94)  (V/V). Adjust the elution rate to approximately 5 mL/min and collect the eluate in a 500-mL K- D flask equipped with a 10-mL concentrator tube. This fraction should contain all of the haloethers.

    - Concentrate the fraction as in Sec- tion 10.6, except use hexane to prewet the column. When the apparatus is cool,  remove the Snyder column and rinse  the  flask  and its lower joint  into  the  concentrator  tube with hexane. Adjust  the  volume  of  the cleaned up extract to 10 mL with hexane and analyze  by  gas  chromatography  (Section  12).

- Gas Chromatography

12.1 Table 1 summarizes the recommended operating conditions for the gas chro- matograph. Included in this table are reten- tion times and MDL that can be achieved under these conditions. Examples of the sep- arations achieved by Columns 1 and 2 are shown in Figures 1 and 2, respectively. Other packed or capillary (open-tubular) columns, chromatographic conditions,  or  detectors may  be  used  if  the  requirements  of  Section

8.2 are met.

  - Calibrate the system daily as de- scribed in Section 7.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 611

  - If the internal standard calibration procedure is being used, the internal stand- ard must be added to the sample extract and

where:

Equation   3

mixed thoroughly immediately before injec- tion into the gas chromatrograph.

  - Inject 2 to 5  L  of  the  sample  extract or  standard  into  the  gas   chromatograph using the solvent-flush  technique. 11  Smaller (1.0 L) volumes may  be  injected  if  auto- matic devices are employed. Record the vol- ume injected to the nearest 0.05 L, the total extract volume, and the  resulting  peak  size in  area  or  peak  height  units.

  - Identify the parameters in the sample by comparing the retention times of the peaks in the sample chromatogram with those of the peaks in standard chromatograms. The width of the retention time window used to make identifications should be based upon measurements of ac- tual retention time variations of standards over the course of a day. Three times the standard deviation of a retention time for a compound can be used to calculate a sug- gested window size; however, the experience of the analyst should weight heavily in the interpretation of chromatograms.

  - If the response for a peak exceeds the working range of the system, dilute the ex- tract and reanalyze.

  - If the measurement of the peak re- sponse is prevented by the presence of inter- ferences, further cleanup is required.

- Calculations

  - Determine the concentration of indi- vidual compounds in the sample.

    - If the external standard calibration procedure is used, calculate the amount of material injected from the peak response using the calibration curve or calibration factor determined in Section 7.2.2. The con- centration in the sample can be calculated from Equation 2.

AVt 

## Concentration (g/L) 

Vi Vs 

Equation   2

where:

A = Amount of material injected (ng). Vi = Volume of extract injected (L). Vt = Volume of total extract (L).

Vs = Volume of water extracted (mL).

    - If the internal standard calibration procedure is used, calculate the concentra- tion in the sample using the response factor (RF) determined in Section 7.3.2 and Equa- tion 3.

As Is 

## Concentration (g/L) 

Ais RFVo 

As  = Response for the parameter to be meas-

ured.

Ais = Response for the internal standard.

Is   =  Amount  of  internal  standard  added  to each extract (g).

Vo = Volume of water extracted (L).

  - Report results in g/L without correc- tion for recovery data. All QC data obtained should be reported with the sample results.

- Method Performance

  - The method detection limit (MDL) is defined as the minimum concentration of a substance that can be measured and reported with 99% confidence that the value is above zero. 1 The MDL concentrations listed  in Table 1 were obtained using reagent water. 12 Similar results were achieved using rep- resentative wastewaters. The MDL actually achieved in a given analysis will vary de- pending on instrument sensitivity and ma- trix  effects.

  - This method has been tested for lin- earity of spike recovery from reagent water and has been demonstrated to be applicable over the concentration range from 4 MDL to 1000 MDL. 12

  - This method was tested by 20 labora- tories using reagent water, drinking water, surface water, and three industrial wastewaters spiked at six concentrations over the range 1.0 to 626 /L. 12 Single oper- ator precision, overall precision, and method accuracy were found to be directly related to the concentration of the parameter and es- sentially independent of the sample matrix. Linear equations to describe these relation- ships are presented in Table 3.

REFERENCES

- 40 CFR part 136, appendix B.

- ‘‘Determination of Haloethers in Indus- trial and Municipal Wastewaters,’’ EPA 600/ 4–81–062, National Technical Information Service, PB81–232290, Springfield, Virginia 22161, July 1981.

- ASTM Annual Book of Standards, Part 31, D3694–78. ‘‘Standard Practices for Prepa- ration of Sample Containers and for Preser- vation of Organic Constitutents,’’ American Society for Testing and Materials, Philadel- phia.

- ‘‘Carcinogens—Working Carcinogens, ’’ Department of Health, Education, and Wel- fare, Public Health Services, Center for Dis- ease Control, National Institute for Occupa- tional Safety and Health, Publication No. 77– 206, August 1977.

- ‘‘OSHA Safety and Health Standards, General Industry,’’ (29 CFR part 1910), Occu- pational Safety and Health Administration, OSHA 2206 (Revised, January 1976).

#### Pt. 136, App. A, Meth. 611

- ‘‘Safety in Academic Chemistry Labora- tories,’’ American Chemical Society Publica- tion, Committee on Chemical Safety, 3rd Edition, 1979.

- Mills., P.A. ‘‘Variation of Florisil Activ- ity: Simple Method for Measuring Absorbent Capacity and Its Use  in  Standardizing Florisil Columns,’’ Journal  of  the  Association of Official Analytical Chemists, 51, 29 (1968).

- Provost,  L.P.,  and  Elder,  R.S.  ‘‘Interpre- tation   of   Percent   Recovery   Data,’’   American Laboratory, 15, 58–63  (1983).  (The  value  2.44 used  in  the  equation  in  Section  8.3.3  is  two times the value 1.22 derived in this report.)

- ASTM Annual Book of Standards, Part 31, D3370–76. ‘‘Standard Practices for Sam- pling Water,’’ American Society for Testing and  Materials,  Philadelphia.

#### 40 CFR Ch. I (7–1–17 Edition)

- ‘‘Methods 330.4 (Titrimetric, DPD-FAS) and 330.5 (Spectrophotometric, DPD) for Chlorine, Total Residual,’’ Methods for Chemical Analysis of Water and Wastes, EPA–600/4–79–020, U.S. Environmental Pro- tection Agency, Environmental Monitoring and Support Laboratory, Cincinnati, Ohio 45268, March 1979.

- Burke, J.A. ‘‘Gas Chromatography for Pesticide Residue Analysis; Some Practical Aspects,’’ Journal of the Association of Official Analytical Chemists, 48, 1037 (1965).

- ‘‘EPA Method Study 21, Method 611, Haloethers,’’ EPA 600/4–84–052, National Technical Information Service, PB84–205939, Springfield, Virginia 22161, June 1984.

TABLE 1—CHROMATOGRAPHIC CONDITIONS AND METHODS DETECTION LIMITS

| Parameters | Retention time (min) | Method detection limit (/L) |
| --- | --- | --- |
|  | Column 1 | Column 2 |  |
| Bis(2-chloroisopropyl) ether ...................................................................................................... | 8.4 | 9.7 | 0.8 |
| Bis(2-chloroethyl) ether ............................................................................................................. | 9.3 | 9.1 | 0.3 |
| Bis(2-chloroethoxy) methane .................................................................................................... | 13.1 | 10.0 | 0.5 |
| 4-Chlorophenyl ether ................................................................................................................. | 19.4 | 15.0 | 3.9 |
| 4-Bromophenyl phenyl ether ..................................................................................................... | 21.2 | 16.2 | 2.3 |

Column 1 conditions: Supelcoport (100/120 mesh) coated with 3% SP–1000 packed in a 1.8 m long 2 mm ID glass column with helium carrier gas at 40 mL/min. flow rate. Column temperature held at 60 C for 2 min. after injection then programmed at 8 C/min. to 230 C and held for 4 min. Under these conditions the retention time for Aldrin is 22.6 min.

Column 2 conditions: Tenax-GC (60/80 mesh) packed in a 1.8 m long 2mm ID glass column with helium carrier gas at 40 mL/min. flow rate. Column temperature held at 150 C for 4 min. after injection then programmed at 16 C/min. to 310 C. Under these conditions the retention time for Aldrin is 18.4 min.

TABLE 2—QC ACCEPTANCE CRITERIA—METHOD 611

| Parameter | Test conc. (g/L) | Limit for s (g/L) | Range for X¯ (g/L) | Range for P, Ps per- cent |
| --- | --- | --- | --- | --- |
| Bis (2-chloroethyl)ether ....................................................................... | 100 | 26.3 | 26.3–136.8 | 11–152 |
| Bis (2-chloroethoxy)methane .............................................................. | 100 | 25.7 | 27.3–115.0 | 12–128 |
| Bis (2-chloroisopropyl)ether ................................................................ | 100 | 32.7 | 26.4–147.0 | 9–165 |
| 4-Bromophenyl phenyl ether ............................................................... | 100 | 39.3 | 7.6–167.5 | D–189 |
| 4-Chlorophenyl phenyl ether ............................................................... | 100 | 30.7 | 15.4–152.5 | D–170 |

s = Standard deviation of four recovery measurements, in g/L (Section 8.2.4). X¯ = Average recovery for four recovery measurements, in g/L (Section 8.2.4).

P, Ps  = Percent recovery measured (Section 8.3.2, Section 8.4.2). D = Detected; result must be greater than zero.

NOTE: These criteria are based directly upon the method performance data in Table 3. Where necessary, the limits for recov- ery have been broadened to assure applicability of the limits to concentrations below those used to develop Table 3.

TABLE 3—METHOD ACCURACY AND PRECISION AS FUNCTIONS OF CONCENTRATION—METHOD 611

| Parameter | Accuracy, as recovery, X (g/L) | Single analyst precision, sr (g/L) | Overall preci- sion, S(g/L) |
| --- | --- | --- | --- |
| Bis(2-chloroethyl) ether ..................................................................................... Bis(2-chloroethoxy) methane ............................................................................ Bis(2-chloroisopropyl) ether .............................................................................. 4–Bromophenyl phenyl ether ............................................................................ 4–Chlorophenyl phenyl ether ............................................................................ | 0.81C + 0.54 0.71C + 0.13 0.85C + 1.67 0.85C + 2.55 0.82C + 1.97 | 0.19X¯ + 0.28 0.20X¯ + 0.15 0.20X¯ + 1.05 0.25X¯ + 0.21 0.18X¯ + 2.13 | 0.35X¯ + 0,36 0.33X¯ + 0.11 0.36X¯ + 0.79 0.47X¯ + 0.37 0.41X¯ + 0.55 |

X= Expected recovery for one or more measuremelts of a sample containing a concentration of C, in g/L.

sr= Expected single analyst standard deviation of measurements at an average concentration found of X¯ , in g/L. S= Expected interlaboratory standard deviation of measurements at an average concentration found of X¯ , in g/L. C = True value for the concentration, in g/L.

X¯ = Average recovery found for measurements of samples containing a concentration of C, in g/L.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 611

Pt. 136, App. A, Meth. 612

40 CFR Ch. I (7–1–17 Edition)

| Parameter | STORET No. | CAS No. |
| --- | --- | --- |
| 2-Chloronaphthalene ....................... | 34581 | 91–58–7 |
| 1,2-Dichlorobenzene ....................... | 34536 | 95–50–1 |
| 1,3-Dichlorobenzene ....................... | 34566 | 541–73–1 |
| 1,4-Dichlorobenzene ....................... | 34571 | 106–46–7 |
| Hexachlorobenzene ........................ | 39700 | 118–74–1 |
| Hexachlorobutadiene ...................... | 34391 | 87–68–3 |
| Hexachlorocyclopentadiene ............ | 34386 | 77–47–4 |
| Hexachloroethane ........................... | 34396 | 67–72–1 |

METHOD   612—CHLORINATED   HYDROCARBONS

- Scope and Application

  - This method covers the determination of certain chlorinated hydrocarbons. The fol- lowing parameters can be determined by this method:

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 612

| Parameter | STORET No. | CAS No. |
| --- | --- | --- |
| 1,2,4-Trichlorobenzene ................... | 34551 | 120–82–1 |

2.2 The method provides a Florisil column cleanup procedure to aid  in  the  elimination of interferences that may be encountered.

3. Interferences

  - This  is  a  gas  chromatographic  (GC)

method  applicable  to  the  determination  of the compounds listed above in municipal and industrial discharges as  provided  under  40 CFR 136.1. When this method is used to  ana- lyze unfamiliar samples for any or all of the compounds above, compound identifications should be supported by  at  least  one  addi- tional qualitative technique. This method describes a second gas chromatographic col- umn that can be used to confirm measure- ments made with the primary  column.  Meth- od 625 provides gas chromatograph/mass spectrometer (GC/MS) conditions  appro- priate for the qualitative and quantitative confirmation of results for all of the param- eters listed above, using the extract  pro- duced  by  this  method.

  - The method detection limit (MDL, de- fined in Section 14.1) 1 for each parameter is listed in Table 1. The MDL for a specific wastewater may differ from those listed, de- pending upon the nature of interferences  in the sample matrix.

  - The sample extraction and concentra- tion steps in this method are essentially the same as in Methods 606, 608, 609, and 611. Thus, a single sample may be extracted to measure the parameters included in the scope of each of these methods. When clean- up is required, the concentration levels must be high enough to permit selecting aliquots, as necessary, to apply appropriate cleanup procedures. The analyst is allowed the lati- tude, under Section 12, to select chromatographic conditions appropriate for the simultaneous measurement of combina- tions of these parameters.

  - Any modification of this method,  be- yond those expressly permitted, shall be con- sidered as a major modification subject to application and approval of alternate test procedures under 40 CFR 136.4 and 136.5.

  - This method is restricted to use by or under the supervision of analysts experi- enced in the use of a gas chromatograph and in the interpretation of gas chromatograms. Each analyst must demonstrate  the  ability to generate acceptable results with this method using the procedure described in Sec- tion 8.2.

- Summary of Method

2.1 A measured volume of sample, ap- proximately 1–L, is extracted with  meth- ylene chloride using a separatory funnel. The methylene chloride extract is dried and ex- changed to hexane during concentration to a volume of 10 mL or less. The extract is sepa- rated by gas chromatography and the param- eters are then measured with an electron capture detector. 2

  - Method interferences may be caused by contaminants in solvents, reagents, glass- ware, and other sample processing hardware that lead to discrete artifacts and/or ele- vated baselines in gas chromatograms. All of these materials must be routinely dem- onstrated to be free from interferences under the conditions of the analysis by running laboratory reagent blanks as described in Section 8.1.3.

    - Glassware must be scrupulously cleaned. 3 Clean all glassware as soon as pos- sible after use by rinsing with the last sol- vent used in it. Solvent rinsing should be fol- lowed by detergent washing with hot water, and rinses with tap water and distilled water. The glassware should then be drained dry, and heated in a muffle furnace at 400 C for 15 to 30 min. Some thermally stable ma- terials, such as PCBs, may not be eliminated by this treatment. Solvent rinses with ace- tone and pesticide quality hexane may be substituted for the muffle furnace heating. Thorough rinsing with such solvents usually eliminates PCB interference. Volumetric ware should not be heated in a muffle fur- nace. After drying and cooling, glassware should be sealed and stored in a clean envi- ronment to prevent any accumulation of dust or other contaminants. Store inverted or capped with aluminum foil.

    - The use of high purity reagents and solvents helps to minimize interference prob- lems. Purification of solvents  by  distillation in all-glass systems may be required.

3.2 Matrix interferences may be caused by contaminants that are co-extracted from the sample. The extent of matrix interferences will vary considerably from source to source, depending upon the nature and diversity  of the industrial complex or municipality being sampled.  The  cleanup  procedure  in  Section

11 can be used to overcome many of these interferences, but unique samples may re- quire additional cleanup approaches to achieve the MDL listed in Table 1.

- Safety

4.1 The toxicity or  carcinogenicity  of each reagent used in this method has not been precisely defined; however, each chem- ical compound should be treated as a poten- tial health hazard. From this viewpoint, ex- posure to these chemicals must be reduced to the lowest possible level by whatever means available. The laboratory is responsible for maintaining a current awareness file of OSHA regulations regarding the safe han- dling of the chemicals specified in this meth- od. A reference file of material data handling sheets should also be made available to all

#### Pt. 136, App. A, Meth. 612

personnel involved in the chemical analysis. Additional  references  to  laboratory  safety are available and have been identified 4M6 for the information of the analyst.

- Apparatus and Materials

  - Sampling equipment, for discrete or composite  sampling.

    - Grab sample bottle—1cL or 1-qt, amber glass, fitted with a screw cap lined with Teflon. Foil may be substituted for Tef- lon if the sample is not corrosive. If amber bottles are not available, protect samples from light. The bottle and cap liner must be washed, rinsed with acetone or methylene chloride, and dried before use to minimize contamination.

    - Automatic sampler (optional)—The sampler must incorporate glass sample con- tainers for the collection of a minimum of 250 mL of sample. Sample containers must be kept refrigerated at 4 C and protected from light during compositing. If the sampler uses a peristaltic pump, a minimum length of compressible silicone rubber tubing may be used. Before use, however, the compressible tubing should be thoroughly rinsed with methanol, followed by repeated rinsings with distilled water to minimize the potential for contamination of the sample. An integrating flow meter is required to collect flow propor- tional  composites.

  - Glassware (All specifications are sug- gested. Catalog numbers are included for il- lustration only.):

    - Separatory funnel—2–L, with Teflon stopcock.

    - Drying column—Chromatographic column, approximately 400 mm long 19 mm ID,  with  coarse  frit  filter  disc.

    - Chromatographic  column—300  long  

10 mm  ID,  with  Teflon  stopcock  and  coarse frit filter disc at bottom.

    - Concentrator tube, Kuderna-Dan- ish—10-mL, graduated (Kontes K–570050–1025 or equivalent). Calibration must  be  checked at the volumes employed in the test. Ground glass stopper is used to prevent evaporation of  extracts.

    - Evaporative flask, Kuderna-Danish— 500-mL (Kontes K–570001–0500 or equivalent). Attach  to  concentrator  tube  with  springs.

    - Snyder column, Kuderna-Danish— Three-ball macro (Kontes K–503000–0121 or equivalent).

    - Vials—10 to 15-mL, amber glass, with Teflon-lined screw cap.

  - Boiling chips—Approximately 10/40 mesh. Heat to 400 C for 30 min or Soxhlet ex- tract  with  methylene  chloride.

  - Water bath—Heated, with concentric ring cover, capable of temperature control (2 C). The bath should be used in a hood.

  - Balance—Analytical, capable of accu- rately weighing 0.0001 g.

  - Gas chromatograph—An analytical system   complete   with   gas   chromatograph

#### 40 CFR Ch. I (7–1–17 Edition)

suitable for on-column injection and all re- quired accessories including syringes, ana- lytical columns, gases, detector, and strip- chart recorder. A data system is rec- ommended for measuring peak areas.

    - Column  1—1.8  m  long  2  mm  ID

glass, packed with 1% SP–1000 on Supelcoport (100/120 mesh) or equivalent. Guidelines for the use of alternate column packings are provide in Section 12.1.

    - Column  2—1.8  m  long  2  mm  ID

glass, packed with 1.5% OV–1/2.4% OV–225 on Supelcoport (80/100 mesh) or equivalent. This column was used to develop the method per- formance statements in Section 14.

    - Detector—Electron capture detector. This detector has proven effective in the analysis of wastewaters for the parameters listed in the scope (Section 1.1), and was used to develop the method performance state- ments in Section 14. Guidelines for the use of alternate detectors are provided in Section 12.1.

- Reagents

  - Reagent water—Reagent water is de- fined as a water in which  an  interferent  is not observed at the  MDL  of  the  parameters of  interest.

  - Acetone, hexane, isooctane, methanol, methylene chloride, petroleum ether (boiling range 30 to 60 C)—Pesticide quality or equiv- alent.

  - Sodium sulfate—(ACS) Granular, an- hydrous. Purify heating at 400 C for 4 h in a shallow  tray.

  - Florisil—PR grade (60/100 mesh). Pur- chase activated at 1250 F and store in the dark in glass containers with ground glass stoppers or foil-lined screw caps. Before use, activate each batch at least 16 h at 130 C in a foil-covered glass container and allow to cool.

  - Stock standard solution (1.00 g/L)— Stock standard solutions can  be  prepared from pure standard materials  or  purchased as certified solutions.

    - Prepare stock standard solutions by accurately weighing about 0.0100 g of pure material. Dissolve  the  material  in  isooctane and dilute to volume in a 120-mL volumetric flask. Larger volumes can be used at the con- venience of the analyst. When compound pu- rity is assayed to be  96%  or  greater,  the weight can be used without correction to cal- culate the concentration of the stock stand- ard. Commercially  prepared  stock  standards can be used at any concentration if they are certified by the manufacturer or by an inde- pendent  source.

    - Transfer the stock standard solu- tions into Teflon-sealed screw-cap bottles. Store at 4 C and protect from light. Stock standard solutions should be checked fre- quently for signs of degradation or evapo- ration, especially just prior to preparing calibration standards from them.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 612

    - Stock standard solutions must be re- placed after six months, or sooner if comparision with  check  standards  indicates a problem.

6.6 Quality control check sample con- centrate—See Section 8.2.1.

- Calibration

  - Establish gas chromatographic oper- ating conditions equivalent to those given in Table 1. The gas chromatographic system can be calibrated using the external standard technique (Section 7.2) or the internal stand- ard technique (Section 7.3).

  - External standard calibration proce- dure:

    - Prepare calibration standards at a minimum of three concentration levels  for each parameter of interest by adding vol- umes of one or more stock standards to a volumetric flask and diluting to volume with isooctane. One of the external standards should be at a concentration near, but above, the MDL (Table 1) and the other concentra- tions should correspond to the expected range of concentrations found in real sam- ples or should define the working range of the detector.

    - Using injections of 2 to 5 L, analyze each calibration standard according to Sec- tion 12 and tabulate peak height or area re- sponses against the mass injected. The re- sults can be used to prepare a calibration curve for each compound. Alternatively, if the ratio of response to amount injected (calibration factor) is a constant over the working range (<10% relative standard devi- ation, RSD), linearity through the origin can be assumed and the average ratio or calibra- tion factor can be used in place of a calibra- tion  curve.

  - Internal standard calibration proce- dure—To use this approach, the analyst must select one or more internal standards that are similar in analytical behavior to the compounds of interest. The analyst must fur- ther demonstrate that the measurement of the internal standard is not affected by method or matrix interferences. Because of these limitations, no internal standard  can be suggested that is applicable to all sam- ples.

    - Prepare calibration standards at a minimum of three concentration levels  for each parameter of interest by adding vol- umes of one or more stock standards to a volumetric flask. To each calibration stand- ard, add a known constant amount of one or more internal standards, and dilute to vol- ume with isooctane. One of the standards should be at a concentration near, but above, the MDL and the other concentrations should correspond to the expected range of concentrations found in real samples or should define the working range of the detec- tor.

    - Using injections of 2 to 5 L, analyze each calibration standard according to Sec- tion 12 and tabulate peak height or area re- sponses against concentration for each com- pound and internal standard. Calculate re- sponse factors (RF) for each compound using Equation 1.

A s C is 

## RF 

Ais Cs 

Equation   1

where:

As  = Response for the parameter to be meas- ured.

Ais = Response for the internal standard.

Cis  = Concentration of the internal standard (g/L).

Cs   =  Concentration  of  the  parameter  to  be measured (g/L).

If the RF value over the working range is a constant (<10% RSD), the RF can be assumed to be invariant and the average RF can be used for calculations. Alternatively, the re- sults can be used to plot a calibration curve of response ratios, As/Ais, vs. RF.

  - The working calibration curve, cali- bration factor, or RF must be verified on each working day by the measurement of one or more calibration standards. If the re- sponse for any parameter varies from the predicted response by more than 15%, a new calibration curve must be prepared for that compound.

  - Before using any cleanup procedure, the analyst must process a series of calibra- tion standards through the procedure to vali- date elution patterns and the absence of interferences from the reagents.

- Quality Control

  - Each laboratory that uses this method is required to operate a formal quality  con- trol program. The minimum requirements of this program consist of an initial demonstra- tion of laboratory capability and an ongoing analysis of spiked samples to evaluate and document data quality. The laboratory must maintain records to document the quality of data that is generated. Ongoing data quality checks are compared with established per- formance criteria to determine if the results of analyses meet the performance character- istics of the method. When the results of sample spikes indicate atypical method per- formance, a quality control check standard must be analyzed to confirm that the meas- urements were performed in an in-control mode of operation.

    - The analyst must make an initial, one-time, demonstration of the ability to generate acceptable accuracy and precision with this method. This  ability  is  established as described in Section 8.2.

#### Pt. 136, App. A, Meth. 612

    - In recognition of advances that are occurring in chromatography, the analyst is permitted certain options (detailed in Sec- tions 10.4, 11.1, and 12.1) to improve the sepa- rations or lower the cost of measurements. Each time such modification is made to the method, the analyst is required to repeat the procedure in Section 8.2.

    - Before processing any samples, the analyst must analyze a  reagent  water  blank to demonstrate that interferences from the analytical system and glassware are under control. Each time a set of samples is ex- tracted or reagents are changed, a reagent water blank must be processed as a safe- guard  against  laboratory  contamination.

    - The laboratory must, on an ongoing basis, spike and analyze a minimum of 10% of all samples to monitor and evaluate lab- oratory data quality. This procedure is de- scribed in Section 8.3.

    - The laboratory must, on an ongoing basis, demonstrate through the analyses of quality control  check standards  that  the op- eration of the measurement system is in con- trol.  This  procedure  is  described  in  Section

8.4. The frequency of the check standard analyses is equivalent to 10% of all samples analyzed but may be reduced if spike recov- eries from samples (Section 8.3) meet all specified quality control criteria.

    - The laboratory must maintain per- formance records to document the quality of data that is generated. This procedure is de- scribed in Section 8.5.

  - To establish the ability to generate acceptable accuracy and precision, the ana- lyst must perform the following operations.

    - A quality control (QC) check sample concentrate is required containing each pa- rameter of interest at the following con- centrations in acetone: Hexachloro-sub- stituted parameters, 10 g/mL; any other chlorinated hydrocarbon, 100 g/mL. The QC check sample concentrate must be obtained from the U.S. Environmental Protection Agency, Environmental Monitoring and Sup- port Laboratory in Cincinnati, Ohio, if avail- able. If not available from  that  source,  the QC check sample concentrate must be ob- tained from another external source. If not available from either source above, the QC check sample concentrate must be prepared by the laboratory using stock standards pre- pared independently from those used for cali- bration.

    - Using a pipet, prepare QC check sam- ples at the test concentrations  shown  in Table 2 by adding 1.00 mL  of  QC  check  sam- ple concentrate to each  of  four  1–L  aliquots of  reagent  water.

    - Analyze the well-mixed QC check samples according to the  method  beginning in Section 10.

    - Calculate the average recovery (X¯ ) in

g/L,  and  the  standard  deviation  of  the  re-

#### 40 CFR Ch. I (7–1–17 Edition)

covery (s) in g/L, for each parameter using the four results.

    - For each parameter compare s and X¯

with the corresponding acceptance criteria for   precision   and   accuracy,   respectively,

found in Table 2. If s and X¯  for all param-

eters of interest meet the acceptance cri- teria, the system performance is acceptable and analysis of actual samples can begin. If any individual s exceeds the precision limit

or any individual X¯  falls outside the range

for accuracy, the system performance is un- acceptable for that parameter.

NOTE: The large number of parameters in Table 2 presents  a  substantial  probability that one or more will fail at least one of the acceptance criteria when all parameters are analyzed.

    - When one or more of the parameters tested fail at least one of the acceptance cri- teria, the analyst must proceed according to Section 8.2.6.1 or 8.2.6.2.

      - Locate and correct the source of the problem and repeat the test for all pa- rameters of interest beginning with Section 8.2.2.

      - Beginning with Section 8.2.2, repeat the test only for those  parameters  that failed to meet criteria. Repeated failure, however, will confirm a  general  problem with the measurement system. If this occurs, locate and correct the source of the problem and repeat the test for all compounds of in- terest beginning with Section 8.2.2.

  - The laboratory must, on an ongoing basis, spike at least 10% of the samples from each sample site being monitored to assess accuracy. For laboratories analyzing one to ten samples per month, at least one spike sample per month is required.

    - The concentration of the spike in the sample should be determined as follows:

      - If, as in compliance monitoring, the concentration of a specific parameter in the sample is being checked against a regu- latory concentration limit, the spike should be at that limit or 1 to 5 times higher than the background concentration determined in Section 8.3.2, whichever concentration would be larger.

      - If the concentration of a specific parameter in the sample  is  not  being checked against a limit specific to that pa- rameter, the spike should be at the test con- centration in Section 8.2.2 or 1 to 5 times higher than the background concentration determined in Section 8.3.2, whichever con- centration would be larger.

      - If it is impractical to determine background levels before spiking (e.g., max- imum holding times will be exceeded), the spike concentration should be (1) the regu- latory concentration limit, if any; or, if none by (2) the larger of either 5 times higher than the expected  background  concentration  or the test concentration in Section 8.2.2.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 612

    - Analyze one sample aliquot to deter- mine the background concentration (B) of each parameter. In necessary, prepare a new QC check sample concentrate (Section 8.2.1) appropriate for the background concentra- tions in the sample. Spike a second sample aliquot with 1.0 mL of the QC check sample concentrate and analyze it to determine the concentration after spiking (A) of each pa- rameter. Calculate each percent recovery (P) as 100 (A¥B)%/T, where T is the known true value of the spike.

    - Compare the percent recovery (P) for each parameter with the corresponding QC acceptance criteria found in Table 2. These acceptance criteria were calculated to  in- clude an allowance for error in measurement of both the background and spike concentra- tions, assuming a spike  to  background  ratio of 5:1. This error will be accounted for to the extent that the analyst’s spike to back- ground ratio approaches 5:1. 7 If spiking was performed at a concentration lower than the test concentration in Section 8.2.2, the ana- lyst must use either the QC acceptance cri- teria in Table 2, or optional QC acceptance criteria calculated for the specific spike con- centration. To calculate optional acceptance criteria for the recovery of a parameter: (1) Calculate accuracy (X) using the equation in Table 3, substituting the spike concentration

(T) for C; (2) calculate overall precision (S) using the equation in Table 3, substituting X for X¯ ; (3) calculate the range for recovery at

the spike concentration  as  (100  X/T)  2.44 (100 S/T)%. 7

    - If any individual P falls outside the designated range for recovery, that param- eter has failed the acceptance criteria. A check standard containing each parameter that failed the criteria must be analyzed as described in Section 8.4.

  - If any parameter fails the acceptance criteria for recovery in Section 8.3, a QC check standard containing each parameter that failed must be prepared and analyzed.

NOTE: The frequency for the required anal- ysis of a QC check standard will depend upon the number of parameters being simulta- neously tested, the complexity of the sample matrix, and the performance of the labora- tory.

    - Prepare the QC check standard by adding 1.0 mL of QC check sample con- centrate (Sections 8.2.1 or 8.3.2) to 1 L of rea- gent water.  The  QC  check  standard  needs only to contain the parameters that failed criteria  in  the  test  in  Section  8.3.

    - Analyze the QC check standard to determine the concentration measured (A) of each parameter. Calculate each percent re- covery (Ps) as 100 (A/T)%, where T is the true value of the standard concentration.

    - Compare the percent recovery (Ps) for each parameter with the corresponding QC acceptance criteria found in Table 2. Only parameters that failed the test in Section 8.3

need to be compared with these criteria. If the recovery of any such parameter falls out- side the designated range, the laboratory performance for that parameter is judged to be out of control, and the problem must be immediately identified and corrected. The analytical result for that parameter in the unspiked sample is suspect and may not be reported for regulatory compliance purposes.

  - As part of the QC program for the lab- oratory, method accuracy for wastewater samples must be assessed and records must be maintained. After the analysis of five spiked wastewater samples as in Section 8.3,

calculate  the  average  percent  recovery  (P¯ )

and the standard deviation of the percent re- covery (sp). Express the  accuracy  assessment as a  percent  recovery  interval  from  P¥2sp  to P + 2sp. If P = 90% and sp = 10%, for example, the accuracy interval is expressed as 70– 110%. Update the accuracy  assessment  for each parameter on a regular basis (e.g. after each five to  ten  new  accuracy  measure- ments).

  - It is recommended that the laboratory adopt additional quality assurance practices for use  with  this method.  The  specific  prac- tices that  are  most  productive  depend  upon the needs of the laboratory and the nature of the samples. Field duplicates may be ana- lyzed to assess the precision of the environ- mental measurements. When doubt exists over the identification of a peak on the chro- matogram, confirmatory techniques such as gas chromatography with a dissimilar col- umn, specific element detector, or mass spectrometer must be used. Whenever pos- sible, the laboratory should analyze standard reference materials and participate  in relevent performance evaluation studies.

- Sample Collection, Preservation, and Handling

  - Grab samples must be collected  in glass containers. Conventional sampling practices 8 should be followed, except  that the bottle must not be prerinsed with sample before collection. Composite samples should be collected in refrigerated  glass  containers in accordance with the requirements of the program. Automatic sampling equipment must be as free as possible of Tygon tubing and other potential sources of contamina- tion.

  - All samples must be iced or refrig- erated at 4 C from the time of collection until   extraction.

  - All samples must be extracted within 7 days of collection and completely analyzed within 40 days of extraction. 2

- Sample Extraction

  - Mark the water meniscus on the side of the sample bottle for later determination of sample volume. Pour the entire sample into a 2–L separatory funnel.

#### Pt. 136, App. A, Meth. 612

  - Add 60 mL of methylele chloride  to the sample bottle, seal, and shake 30 s to rinse the inner surface. Transfer the solvent to the separatory funnel and extract the sample by shaking the funnel for 2 min with periodic venting to release excess pressure. Allow the organic layer to separate from the water phase for a minimum of 10 min. If the emulsion interface between layers is more than one-third the volume of  the  solvent layer, the analyst must employ mechanical techniques to complete the phase separation. The optimum technique depends upon the sample, but may include  stirring,  filtration of the emulsion through glass wool, cen- trifugation, or other physical methods. Col- lect the methylene chloride extract in a 250- mL  Erlenmeyer  flask.

  - Add a second 60-mL volume of meth- ylene chloride to the sample bottle and re- peat the extraction procedure a second time, combining the extracts in the Erlenmeyer flask. Perform a third extraction in the same manner.

  - Assemble a Kuderna-Danish (K-D) concentrator by attaching a 10-mL concen- trator tube to a 500-mL evaporative flask. Other concentration devices or  techniques may be used in place of the K-D concentrator if the requirements of Section 8.2 are met.

  - Pour the combined extract through a solvent-rinsed drying column containing about 10 cm of anhydrous sodium sulfate, and collect the extract in the K-D concen- trator. Rinse the Erlenmeyer flask and col- umn with 20 to 30 mL of methylene chloride to complete the quantitative transfer.

  - Add one or two clean boiling chips to the evaporative flask and attach a three-ball Snyder column. Prewet the Snyder  column by adding about 1 mL of methylene chloride to the top. Place the K-D apparatus on a hot water bath (60 to 65 C) so that the concen- trator tube is partially immersed in the hot water, and the entire lower rounded surface of the flask is bathed with hot vapor. Adjust the vertical position of the apparatus  and the water temperature as required to com- plete the concentration in 15 to  20  min.  At the proper rate of distillation the balls of the column will actively chatter but the cham- bers will not flood with condensed solvent. When the apparent volume of liquid reaches

1  to  2  mL,  remove  the  K-D  apparatus  and allow it to drain and cool for at least 10 min. NOTE:  The  dichloribenzenes  have  a  suffi- ciently  high  volatility  that  significant  losses may  occur  in  concentration  steps  if  care  is not  exercised.  It  is  important  to  maintain  a constant  gentle  evaporation  rate  and  not  to allow the liquid volume to fall below 1 to 2 mL before removing the K-D apparatus from

the hot water bath.

  - Momentarily remove the Snyder col- umn, add 50 mL of hexane and a new boiling chip, and reattach the Snyder column.  Raise the tempeature of the water bath to 85 to 90

#### 40 CFR Ch. I (7–1–17 Edition)

C. Concentrate the  extract  as  in  Section 10.6, except use hexane to prewet the column. The elapsed  time  of  concentration  should  be 5 to 10 min.

  - Romove the Snyder column and rinse the flask and its lower joint into the concen- trator tube with 1 to 2 mL of hexane. A 5-mL syringe is recommended for this operation. Stopper the concentrator tube and store re- frigerated if further processing will not be performed immediately. If the extract  will be stored longer than two days, it should be transferred to a Teflon-sealed screw-cap vial. If the sample extract requires no further cleanup, proceed with gas chromatographic analysis (Section 12). If the sample requires further cleanup, proceed to Section 11.

  - Determine the original sample vol- ume by refilling the sample bottle to the mark and transferring the liquid to  a  1000- mL graduated cylinder. Record the sample volume to the nearest 5 mL.

- Cleanup and Separation

  - Cleanup procedures may not be nec- essary for a relatively clean sample matrix. If particular circumstances demand the use of a cleanup procedure, the analyst may use the procedure below or any other appropriate procedure. However, the analyst first must demonstrate that the requirements of Sec- tion 8.2 can be met using the method as re- vised to incorporate the cleanup procedure.

  - Florisil column cleanup for chlorinated hydrocarbons:

    - Adjust the sample extract to 10 mL with hexane.

    - Place 12 g of Florisil into a chromatographic column. Tap the column to settle the Florisil and add 1 to 2 cm of anhy- drous sodium sulfate to the top.

    - Preelute the column with 100 mL of petroleum ether. Discard the eluate and just prior to exposure of the sodium sulfate layer to the air, quantitatively transfer the  sam- ple extract onto the column by decantation and subsequent petroleum ether washings. Discard the eluate. Just prior to exposure of the sodium sulfate layer to the air, begin eluting the column with 200 mL of petroleum ether and collect the eluate in a 500-mL K-D flask equipped with a 10-mL concentrator tube. This fraction should contain all of the chlorinated  hydrocarbons.

    - Concentrate the fraction as in Sec- tion 10.6, except use hexane to prewet the column. When the apparatus is cool, remove the Snyder column and rinse the flask and its lower joint into the concentrator tube with hexane. Analyze by gas chroma- tography (Section 12).

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 612

- Gas Chromatography

  - Table 1 summarizes the recommended operating conditions for the gas chro- matograph. Included in this table are reten- tion times and MDL that can be achieved under these conditions. Examples of the sep- arations achieved by Columl 2 are shown in Figures 1 and 2. Other packed or capillary (open-tubular) columns, chromatographic conditions, or detectors may be used if the requirements of Section 8.2 are met.

  - Calibrate the system daily as de- scribed in Section 7.

  - If the internal standard calibration procedure is being used, the internal stand- ard must be added to the sample extract and mixed throughly immediately before injec- tion into the gas chromatograph.

  - Inject 2 to 5  L  of  the  sample  extract or  standard  into  the  gas   chromatograph using the  solvent-flush  techlique. 9  Smaller (1.0 L) volumes may  be  injected  if  auto- matic devices are employed. Record the vol- ume injected to the nearest 0.05 L, the total extract volume, and the  resulting  peak  size in  area  or  peak  height  units.

  - Identify the parameters in the sample by comparing the retention times of the peaks in the sample chromatogram with those of the peaks in standard chromatograms. The width of the retention time window used to make identifications should be based upon measurements of ac- tual retention time variations of standards over the course of a day. Three times the standard deviation of a retention time for a compound can be used to calculate a sug- gested window size; however, the experience of the analyst should weigh heavily in the interpretation of chromatograms.

  - If the response for a peak exceeds the working range of the system, dilute the ex- tract and reanalyze.

  - If the measurement of the peak re- sponse is prevented by the presence of inter- ferences, further cleanup is required.

- Calculations

  - Determine the concentration of indi- vidual compounds in the sample.

    - If the external standard calibration procedure is used, calculate the amount of material injected from the peak response using the calibration curve or calibration factor determined in Section 7.2.2. The con- centration in the sample can be calculated from Equation 2.

AVt 

## Concentration (g/L) 

Vi Vs 

Equation   2

where:

A = Amount of material injected (ng).

Vi = Volume of extract injected (L). Vt = Volume of total extract (L).

Vs = Volume of water extracted (mL).

    - If the internal standard calibration procedure is used, calculate the concentra- tion in the sample using the response factor (RF) determined in Section 7.3.2 and Equa- tion 3.

	A s I s 

## Concentration (g/L) 

Ais RFVo 

Equation   3

where:

As  = Response for the parameter to be meas- ured.

Ais = Response for the internal standard.

Is   =  Amount  of  internal  standard  added  to each extract (g).

Vo = Volume of water extracted (L).

13.2 Report results in g/L without correc- tion for recovery data. All QC data obtained should be reported with the sample results.

- Method Performance

  - The method detection limit (MDL) is defined as the minimum concentration of a substance that can be measured and reported with 99% confidence that the value is above zero. 1 The MDL concentrations listed  in Table 1 were obtained using reagent water. 10 Similar results were achieved using rep- resentative wastewaters. The MDL actually achieved in a given analysis will vary de- pending on instrument sensitivity and ma- trix  effects.

  - This method has been tested for lin- earity of spike recovery from reagent water and has been demonstrated to be applicable over the concentration range from 4 MDL to 1000 MDL. 10

  - This method was tested by 20 labora- tories using reagent water, drinking water, surface water, and three industrial wastewaters spiked at six concentrations over the range 1.0 to 356 g/L. 11 Single oper- ator precision, overall precision, and method accuracy were found to be directly related to the concentration of the parameter and es- sentially independent of the sample matrix. Linear equations to describe these relation- ships are presented in Table 3.

REFERENCES

- 40 CFR part 136, appendix B.

- ‘‘Determination of Chlorinated Hydro- carbons In Industrial and Municipal Wastewaters, ‘‘EPA 6090/4–84–ABC, National Technical Information Service, PBXYZ, Springfield, Virginia, 22161 November 1984.

- ASTM Annual Book of Standards, Part 31, D3694–78. ‘‘Standard Practices for Prepa- ration of Sample Containers and for Preser- vation   of   Organic   Constituents,’’   American

#### Pt. 136, App. A, Meth. 612

Society for Testing and Materials, Philadel- phia.

- ‘‘Carcinogens—Working With Carcino- gens,’’ Department of Health, Education, and Welfare, Public Health Service, Center for Disease Control, National Institute for Occu- pational Safety and Health, Publication No. 77–206, August 1977.

- ‘‘OSHA Safety and Health Standards, General Industry,’’ (29 CFR part 1910), Occu- pational Safety and Health Administration, OSHA 2206 (Revised, January 1976).

- ‘‘Safety in Academic Chemistry Labora- tories,’’ American Chemical Society Publica- tion, Committee on Chemical Safety, 3rd Edition, 1979.

- Provost,  L.P.,  and  Elder,  R.S.  ‘‘Interpre- tation    of    Percent    Recovery    Data,’’American Laboratory, 15, 58–63  (1983).  (The  value  2.44 used  in  the  equation  in  Section  8.3.3  is  two times the value 1.22 derived in this report.)

- ASTM Annual Book of Standards, Part 31,  D3370–76.  ‘‘Standard  Practices  for  Sam-

#### 40 CFR Ch. I (7–1–17 Edition)

pling Water,’’ American Society for Testing and Materials, Philadelphia.

- Burke, J.A. ‘‘Gas Chromatography for Pesticide Residue Analysis; Some Practical Aspects,’’ Journal of the Association of Official Analytical Chemists, 48, 1037 (1965).

- ‘‘Development of Detection Limits, EPA Method 612, Chlorinated Hydro- carbons,’’ Special letter report for EPA Con- tract 68–03–2625, U.S. Environmental Protec- tion Agency, Environmental Monitoring and Support Laboratory, Cincinnati, Ohio 45268.

- ‘‘EPA Method Study Method 612— Chlorinated Hydrocarbons,’’  EPA  600/4–84– 039, National Technical Information Service, PB84–187772, Springfield, Virginia 22161, May 1984.

- ‘‘Method	Performance	for Hexachlorocyclopentadiene by Method 612,’’ Memorandum from R. Slater, U.S. Environ- mental Protection Agency, Environmental Monitoring and Support Laboratory, Cin- cinnati, Ohio 45268, December 7, 1983.

TABLE 1—CHROMATOGRAPHIC CONDITIONS AND METHOD DETECTION LIMITS

| Parameter | Retention time (min) | Method de- tection limit (g/L) |
| --- | --- | --- |
|  | Column 1 | Column 2 |  |
| 1,3-Dichlorobenzene ..................................................................................................... | 4.5 | 6.8 | 1.19 |
| Hexachloroethane ......................................................................................................... | 4.9 | 8.3 | 0.03 |
| 1,4-Dichlorobenzene ..................................................................................................... | 5.2 | 7.6 | 1.34 |
| 1,2-Dichlorobenzene ..................................................................................................... | 6.6 | 9.3 | 1.14 |
| Hexachlorobutadiene ..................................................................................................... | 7.7 | 20.0 | 0.34 |
| 1,2,4-Trichlorobenzene .................................................................................................. | 15.5 | 22.3 | 0.05 |
| Hexachlorocyclopentadiene .......................................................................................... | nd | c 16.5 | 0.40 |
| 2-Chloronaphthalene ..................................................................................................... | a 2.7 | b 3.6 | 0.94 |
| Hexachlorobenzene ....................................................................................................... | a 5.6 | b 10.1 | 0.05 |

Column 1 conditions: Supelcoport (100/120 mesh) coated with 1% SP–1000 packed in a 1.8 m 2 mm ID glass column with 5% methane/95% argon carrier gas at 25 mL/min. flow rate. Column temperature held isothermal at 65 C, except where other- wise indicated.

Column 2 conditions: Supelcoport (80/100 mesh) coated with 1.5% OV–1/2.4% OV–225 packed in a 1.8 m 2 mm ID glass column with 5% methane/95% argon carrier gas at 25 mL/min. flow rate. Column temperature held isothermal at 75 C, except where otherwise indicated.

nd = Not determined.

a 150 C column temperature. b 165 C column temperature. c 100 C column temperature.

TABLE 2—QC ACCEPTANCE CRITERIA—METHOD 612

| Parameter | Test conc. (g/ L) | Limit for s (g/L) | Range for X¯ (g/L) | Range for P, Ps (percent) |
| --- | --- | --- | --- | --- |
| 2-Chloronaphthalene ......................................................................................... | 100 | 37.3 | 29.5–126.9 | 9–148 |
| 1,2-Dichlorobenzene ......................................................................................... | 100 | 28.3 | 23.5–145.1 | 9–160 |
| 1,3-Dichlorobenzene ......................................................................................... | 100 | 26.4 | 7.2–138.6 | D–150 |
| 1,4-Dichlorobenzene ......................................................................................... | 100 | 20.8 | 22.7–126.9 | 13–137 |
| Hexachlorobenzene .......................................................................................... | 10 | 2.4 | 2.6–14.8 | 15–159 |
| Hexachlorobutadiene ........................................................................................ | 10 | 2.2 | D–12.7 | D–139 |
| Hexachlorocyclopentadiene .............................................................................. | 10 | 2.5 | D–10.4 | D–111 |
| Hexachloroethane ............................................................................................. | 10 | 3.3 | 2.4–12.3 | 8–139 |
| 1,2,4-Trichlorobenzene ..................................................................................... | 100 | 31.6 | 20.2–133.7 | 5–149 |

s = Standard deviation of four recovery measurements, in g/L (Section 8.2.4). X¯ = Average recovery for four recovery measurements, in g/L (Section 8.2.4).

P, Ps  = Percent recovery measured (Section 8.3.2, Section 8.4.2). D = Detected; result must be greater than zero.

NOTE: These criteria are based directly upon the method performance data in Table 3. Where necessary, the limits for recov- ery have been broadened to assure applicability of the limits to concentrations below those used to develop Table 3.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 612

TABLE 3—METHOD ACCURACY AND PRECISION AS FUNCTIONS OF CONCENTRATION—METHOD 612

| Parameter | Acccuracy, as recovery, X (g/L) | Single analyst precision, sr (g/L) | Overall preci- sion, S(g/L) |
| --- | --- | --- | --- |
| 2-Chloronaphthalene ......................................................................................... | 0.75C + 3.21 | 0.28X¯ ¥1.17 | 0.38X¯ ¥1.39 |
| 1,2-Dichlorobenzene ......................................................................................... | 0.85C¥0.70 | 0.22X¯ ¥2.95 | 0.41X¯ ¥3.92 |
| 1,3-Dichlorobenzene ......................................................................................... | 0.72C + 0.87 | 0.21X¯ ¥1.03 | 0.49X¯ ¥3.98 |
| 1,4-Dichlorobenzene ......................................................................................... | 0.72C + 2.80 | 0.16X¯ ¥0.48 | 0.35X¯ ¥0.57 |
| Hexachlorobenzene ........................................................................................... | 0.87C¥0.02 | 0.14X¯ + 0.07 | 0.36X¯ ¥0.19 |
| Hexachlorobutadiene ......................................................................................... | 0.61C + 0.03 | 0.18X¯ + 0.08 | 0.53X¯ ¥0.12 |
| Hexachlorocyclopentadiene a ............................................................................ | 0.47C | 0.24X¯ | 0.50X¯ |
| Hexachloroethane ............................................................................................. | 0.74C¥0.02 | 0.23X¯ + 0.07 | 0.36X¯ ¥0.00 |
| 1,2,4-Trichlorobenzene ...................................................................................... | 0.76C + 0.98 | 0.23X¯ ¥0.44 | 0.40X¯ ¥1.37 |

X= Expected recovery for one or more measurements of a sample containing a concentration of C, in g/L.

sr= Expected single analyst standard deviation of measurements at an average concentration found of X¯ , in g/L. S= Expected interlaboratory standard deviation of measurements at an average concentration found of X¯ , in g/L. C = True value for the concentration, in g/L.

X¯ = Average recovery found for measurements of samples containing a concentration of C, in g/L.

a Estimates based upon the performance in a single laboratory. 12

#### Pt. 136, App. A, Meth. 612

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 612

Pt. 136, App. A, Meth. 613

METHOD  613—2,3,7,8-TETRACHLORODIBENZO-P- DIOXIN

- Scope and Application

  - This method covers the determination of 2,3,7,8-tetrachlorodibenzo-p-dioxin (2,3,7,8- TCDD). The following parameter may be de- termined by this method:

| Parameter | STORET No. | GAS No. |
| --- | --- | --- |
| 2,3,7,8-TCDD ................................ | 34675 | 1746–01–6 |

  - This is a gas chromatographic/mass spectrometer (GC/MS)  method  applicable  to the determination of 2,3,7,8–TCDD in munic- ipal and industrial discharges as provided under 40 CFR 136.1. Method 625 may be used to screen samples for 2,3,7,8–TCDD. When the screening test is positive, the  final  quali- tative  confirmation  and  quantification  must be made using Method 613.

  - The method detection limit (MDL, de- fined in Section 14.1) 1 for 2,3,7,8–TCDD is listed in Table 1. The MDL for a specific wastewater may be different from  that  list- ed, depending upon the nature of inter- ferences in the sample matrix.

  - Because of the extreme toxicity of this compound, the analyst must prevent expo- sure to himself, of to others, by materials knows or believed to contain 2,3,7,8–TCDD. Section 4 of this method contains guidelines and protocols that serve as minimum safe- handling standards in a limited-access lab- oratory.

  - Any modification of this method,  be- yond those expressly permitted, shall be con- sidered as a major modification subject to application and approval of alternate test procedures under 40 CFR 136.4 and 136.5.

  - This method is restricted to use by or under the supervision of analysts experi- enced in  the  use  of  a  gas  chromatograph/ mass spectrometer and in the interpretation of mass spectra. Each analyst must dem- onstrate the ability to generate acceptable results with this method using the procedure described in Section 8.2.

- Summary of Method

  - A measured volume of sample, ap- proximately 1–L, is spiked with an internal standard of labeled 2,3,7,8–TCDD and ex- tracted with methylene chloride using a separatory funnel. The methylene chloride extract is exchanged to hexane during con- centration to a volume of 1.0 mL or less. The extract is then analyzed by capillary column GC/MS to separate and measure 2,3,7,8– TCDD. 2 3

  - The method provides selected column chromatographic cleanup proceudres to aid in the elimination of interferences that may be encountered.

#### 40 CFR Ch. I (7–1–17 Edition)

- Interferences

  - Method interferences may be caused by contaminants in solvents, reagents, glass- ware, and other sample processing hardware that lead to discrete artifacts  and/or  ele- vated backgrounds at the masses (m/z) mon- itored. All of these materials must be rou- tinely demonstrated to be free from inter- ferences under the conditions of the analysis by running laboratory reagent blanks as de- scribed in Section 8.1.3.

    - Glassware must be scrupulously cleaned. 4 Clean all glassware as soon as pos- sible after use by rinsing with the last sol- vent used in it. Solvent rinsing should be fol- lowed by detergent washing with hot water, and rinses with tap water and distilled water. The glassware should then be drained dry, and heated in a muffle furnace at 400 C for 15 to 30 min. Some thermally stable ma- terials, such as PCBs, may not be eliminated by the treatment. Solvent rinses with ace- tone and pesticide quality hexane may be substituted for the muffle furnace heating. Thorough rinsing with such solvents usually eliminates PCB interference. Volumetric ware should not be heated in a muffle fur- nace. After drying and cooling, glassware should be sealed and stored in a clean envi- ronment to prevent any accumulation of dust or other contaminants. Store inverted or capped with aluminum foil.

    - The use of high purity reagents and solvents helps to mininmize interference problems. Purification of solvents by dis- tillation in all-glass systems may be re- quired.

  - Matrix interferences may be caused by contaminants  that  are  coextracted  from  the sample.  The  extent  of  matrix  interferences will vary considerably from source to source, depending  upon  the  nature  and  diversity  of the industrial complex or municipality being sampled.   2,3,7,8–TCDD   is   often   associated with    other    interfering    chlorinated    com- pounds  which  are  at  concentrations  several magnitudes higher than that of 2,3,7,8–TCDD. The cleanup producers in Section 11 can be used   to   overcome   many   of   these   inter- ferences, but unique samples may require ad- ditional  cleanup  approaches 1 5M7    to  elimi- nate   false   positives   and   achieve   the   MDL listed in Table 1.

  - The primary column, SP–2330 or equiv- alent,  resolves  2,3,7,8–TCDD  from  the  other

21 TCDD  insomers.  Positive  results  using any other gas chromatographic column must be confirmed using the primary column.

- Safety

  - The toxicity or carcinogenicity of each reagent used in this method has not been precisely defined; however, each chem- ical compound should be treated as a poten- tial health hazard. From this viewpoint, ex- posure to these chemicals must be reduced to

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 613

the lowest possible level by whatever means available. The laboratory is responsible for maintaining   a   current   awareness   file   of OSHA  regulations  regarding  the  safe  han- dling of the chemicals specified in this meth- od. A reference file of material data handling sheets should also be made available to all personnel involved in the chemical analysis. Additional  references  to  laboratory  safety are available and have been identified 8M10 for the information of the analyst. Benzene and 2,3,7,8–TCDD have been identified as sus- pected human or mammalian carcinogens.

  - Each laboratory must develop a strict safety program for handling 2,3,7,8–TCDD. The following laboratory practices are rec- ommended:

    - Contamination of the laboratory will be minimized by conducting all manipula- tions in a hood.

    - The effluents of sample splitters for the gas chromatograph and roughing pumps on the GC/MS should pass through either a column of activated charcoal or be bubbled through a trap containing oil or high-boiling alcohols.

    - Liquid waste should be dissolved in methanol or ethanol and irradiated with ul- traviolet light with a  wavelength  greater than 290 nm for several days. (Use F 40 BL lamps or equivalent). Analyze liquid wastes and dispose of the solutions when 2,3,7,8– TCDD can no longer be detected.

  - Dow Chemical U.S.A. has issued the following precautimns (revised November 1978) for safe handling of 2,3,7,8–TCDD in the laboratory:

    - The following statements on safe handling are as complete as possible on the basis of available toxicological information. The precautions for safe handling and  use are necessarily general in nature since de- tailed, specific recommendations  can  be made only for the particular exposure and circumstances of each individual use. Inquir- ies about specific operations or uses may be addressed to the Dow Chemical Company. Assistance in evaluating the  health  hazards of particular plant conditions may be ob- tained from certain consulting laboratories and from State Departments of Health or of Labor, many of which have an  industrial health service. 2,3,7,8–TCDD is extremely toxic to laboratory animals. However, it has been handled for years without injury in an- alytical and biological laboratories. Tech- niques used in handling radioactive and in- fectious materials are applicable to 2,3,7,8,– TCDD.

      - Protective	equipment—Throw- away plastic gloves, apron or lab coat, safety glasses, and a lab hood adequate for radio- active  work.

      - Training—Workers must be trained in the proper method of removing contami- nated gloves and  clothing  without  con- tacting  the  exterior  surfaces.

      - Personal hygiene—Thorough wash- ing of hands and forearms after each manipu- lation and before breaks (coffee, lunch, and shift).

      - Confinement—Isolated work area, posted with signs, segregated glassware and tools, plastic-backed  absorbent  paper  on benchtops.

      - Waste—Good technique includes minimizing contaminated waste. Plastic bag liners should be used in waste cans. Janitors must be trained in the safe handling of waste.

      - Disposal of wastes—2,3,7,8–TCDD decomposes above 800 C. Low-level waste such as absorbent paper, tissues, animal re- mains, and plastic gloves may be burned in a good incinerator. Gross quantities (milli- grams) should be packaged securely and dis- posed through commercial or governmental channels which are capable of handling high- level radioactive wastes or extremely toxic wastes. Liquids should be allowed to evapo- rate in a good hood and in a disposable con- tainer. Residues may then be handled as above.

      - Decontamination—For personal de- contamination, use any mild soap with plen- ty of scrubbing action. For decontamination of glassware, tools, and  surfaces, Chlorothene NU Solvent (Trademark of the Dow Chemical Company) is the least toxic solvent shown to be effective. Satisfactory cleaning may be accomplished by rinsing with Chlorothene, then washing with any de- tergent and water. Dishwater may be dis- posed to the sewer. It is prudent to minimize solvent wastes because they may require spe- cial disposal through commercial sources which are expensive.

      - Laundry—Clothing known to be contaminated should be disposed with the precautions described under Section 4.3.1.6. Lab coats or other clothing worn in 2,3,7,8– TCDD work areas may be laundered.

Clothing should be collected in  plastic bags. Persons who convey the bags and laun- der the clothing should be advised of the haz- ard and trained in proper handling. The clothing may be put into a washer without contact if the launderer knows the problem. The washer should be run through a cycle be- fore being used again for other clothing.

      - Wipe tests—A useful method of de- termining cleanliness of work  surfaces  and tools is to wipe the surface with a piece  of filter paper. Extraction and analysis by gas chromatography can achieve a limit of sensi- tivity of 0.1 g per wipe. Less than 1 g of 2,3,7,8–TCDD per sample indicates acceptable cleanliness;  anything  higher  warrants   fur- ther cleaning. More than 10 g on a wipe sample constitutes an acute hazard and re- quires prompt cleaning before further use  of the equipment or work space. A high (>10 g)

#### Pt. 136, App. A, Meth. 613

2,3,7,8–TCDD level indicates that unaccept- able work practices have been employed  in the  past.

      - Inhalation—Any procedure that may produce airborne contamination must be done with good ventilation. Gross losses to a ventilation system must not be allowed. Handling of the dilute solutions normally used in analytical and animal work presents no inhalation hazards except in the case of an accident.

      - Accidents—Remove contaminated clothing  immediately,  taking  precautions not to contaminate skin or other articles. Wash exposed skin vigorously and repeatedly until  medical  attention  is  obtained.

- Apparatus and Materials

  - Sampling equipment, for discrete or composite  sampling.

    - Grab sample bottle—1–L or 1-qt, amber glass, fitted with a screw cap lined with Teflon. Foil may be substituted for Tef- lon if the sample is not corrosive. If amber bottles are not available, protect samples from light. The bottle and cap liner must be washed, rinsed with acetone or methylene chloride, and dried before use to minimize contamination.

    - Automatic sampler (optional)—The sampler must incorporate glass sample con- tainers for the collection of a minimum of 250 mL of sample. Sample containers must be kept refrigerated at 4 C and protected from light during compositing. If the sampler uses a peristaltic pump, a minimum length of compressible silicone rubber tubing may be used. Before use, however, the compressible tubing should be thoroughly rinsed with methanol, followed by repeated rinsings with distilled water to minimize the potential for contamination of the sample. An integrating flow meter is required to collect flow propor- tional  composites.

    - Clearly  label  all  samples  as  ‘‘POI- SON’’ and ship according to U.S. Department of Transportation regulations.

  - Glassware (All specifications are sug- gested. Catalog numbers are included for il- lustration only.):

    - Separatory funnels—2–L and 125-mL, with Teflon stopcock.

    - Concentrator tube, Kuderna-Dan- ish—10-mL, graduated (Kontes K–570050–1025 or equivalent). Calibration must  be  checked at the volumes employed in the test. Ground glass stopper is used to prevent evaporation of  extracts.

    - Evaporative flask, Kuderna-Danish— 500–mL (Kontes K–570001–0500 or equivalent). Attach  to  concentrator  tube  with  springs.

    - Snyder column, Kuderna-Danish— Three-ball macro (Kontes K–503000–0121 or equivalent).

    - Snyder column, Kuderna-Danish— Two-ball micro (Kontes K–569001–0219 or equivalent).

#### 40 CFR Ch. I (7–1–17 Edition)

    - Vials—10 to 15–mL, amber glass, with Teflon-lined screw cap.

    - Chromatographic column—300 mm long 10 mm ID, with Teflon stopcock and coarse frit filter disc at bottom.

    - Chromatographic column—400 mm long 11 mm ID, with Teflon stopcock and coarse frit filter disc at bottom.

  - Boiling chips—Approximately 10/40 mesh. Heat to 400 C for 30 min or Soxhlet ex- tract  with  methylene  chloride.

  - Water bath—Heated, with concentric ring cover, capable of temperature control (2 C). The bath should be used in a hood.

  - GC/MS system:

    - Gas chromatograph—An analytical system complete  with  a  temperature  pro- grammable gas chromatograph and all re- quired accessories including syringes, ana- lytical columns, and gases.  The  injection port must be designed for capillary columns. Either split, splitless, or on-column injection techniques may be employed, as long as the requirements of Section 7.1.1 are achieved.

    - Column—60   m   long   0.25   mm   ID

glass or fused silica, coated with SP–2330 (or equivalent) with a film thickness of 0.2 m. Any equivalent column must resolve 2, 3, 7, 8–TCDD from the other 21 TCDD isomers. 16

    - Mass spectrometer—Either a low res- olution mass spectrometer (LRMS) or a high resolution mass spectrometer (HRMS) may be used. The mass spectrometer must be equipped with a 70 V (nominal) ion  source and be capable of aquiring m/z abundance data in real  time selected ion  monitoring (SIM) for groups of four or more masses.

    - GC/MS interface—Any GC to MS interface can be used that achieves the re- quirements of Section 7.1.1. GC to MS inter- faces constructed of all glass or glass-lined materials are recommended. Glass surfaces can be deactivated by silanizing with dichlorodimethylsilane. To achieve max- imum sensitivity, the exit end of the cap- illary column should be placed in the ion source. A short piece of fused silica capillary can be used as the interface to overcome problems associated with straightening the exit end of glass capillary columns.

    - The SIM data acquired during the chromatographic program is defined as the Selected Ion Current Profile  (SICP).  The SICP can be acquired under computer con- trol or as a real time analog output. If com- puter control is used, there must be software available to plot the SICP and report peak height or area data for any m/z in the SICP between specified time or scan number lim- its.

  - Balance—Analytical, capable of accu- rately weighing 0.0001 g.

- Reagents

  - Reagent water—Reagent water is de- fined as a water in which an  interferent  is not observed at the MDL of 2, 3, 7, 8–TCDD.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 613

  - Sodium hydroxide solution (10 N)— Dissolve 40 g of NaOH (ACS) in reagent water and dilute to 100 mL. Wash the solution with methylene chloride and hexane before use.

  - Sodium thiosulfate—(ACS) Granular.

  - Sulfuric acid—Concentrated (ACS, sp. gr. 1.84).

  - Acetone, methylene chloride, hexane, benzene, ortho-xylene, tetradecane—Pes- ticide  quality  or  equivalent.

  - Sodium sulfate—(ACS) Granular, an- hydrous. Purify by heating at 400 C for 4 h in a shallow tray.

  - Alumina—Neutral, 80/200 mesh (Fisher Scientific Co., No. A–540 or equivalent). Be- fore use, activate for 24 h at 130 C in a foil- covered  glass  container.

  - Silica gel—High purity grade, 100/120 mesh (Fisher Scientific Co., No. S–679 or equivalent).

  - Stock standard solutions (1.00 g/L)— Stock standard solutimns can be prepared from pure standard materials  or  purchased as certified solutions. Acetone  should  be used as  the  solvent  for  spiking solutions; ortho-xylene is recommended for calibration standards for split injectors; and tetradecane is recommended  for  splitless  or  on-colum injectors.  Analyze  stock  internal   standards to verify the absence of native 2,3,7,8–TCDD.

    - Prepare stock standard solutions of 2,3,7,8–TCDD (mol wt 320) and either 37C14 2,3,7,8–TCDD (mol wt 328) or 13C112 2,3,7,8– TCDD (mol wt 332) in an isolated area by ac- curately weighing about 0.0100 g of pure ma- terial. Dissolve the  material  in  pesticide quality solvent and dilute to volume  in  a  10- mL volumetric flask.  When  compound  purity is assayed to be 96% or greater,  the  weight can be used without correction to  calculate the concentration of the stock standard. Commercially  prepared  stock  standards  can be used at any concentration if they are cer- tified by the manufacturer or by an inde- pendent  source.

    - Transfer the stock standard solu- tions into Teflon-sealed screw-cap bottles. Store in an isolated refrigerator protected from light. Stock standard solutions should be checked frequently for signs of degrada- tion or evaporation, especially just prior to preparing calibration standards or spiking solutions from them.

    - Stock standard solutions must be re- placed after six months, or sooner if com- parison with check standards indicates a problem.

  - Internal standard spiking solution (25 ng/mL)—Using stock standard solution, pre- pare a spiking  solution  in  acetone  of  either 13 Cl12 or 37 Cl4 2,3,7,8–TCDD at a concentra- tion of 25 ng/mL. (See Section 10.2)

  - Quality control check sample con- centrate—See Section 8.2.1.

- Calibration

  - Establish  gas  chromatograhic  oper- ating conditions equivalent to those given in Table 1 and SIM conditions for the mass spectrometer as described in Section 12.2 The GC/MS system must be calibrated using the internal   standard   technique.

    - Using stock standards, prepare cali- bration standards that will allow measure- ment of  relative  response  factors  of  at least three concentration ratios of 2,3,7,8–TCDD to internal standard. Each calibration standard must be prepared  to contain  the internal standard at a concentration of 25 ng/mL.  If any interferences are contributed by the in- ternal standard at m/z 320 and 322, its con- centration may be reduced in the calibration standards and in the internal standard spik- ing solution (Section 6.10). One of the cali- bration standards should contain 2,3,7,8– TCDD at a concentration near, but  above, the MDL and the other 2,3,7,8–TCDD con- centrations should correspond to the ex- pected range of concentrations found in real samples or should define the working range of the GC/MS system.

    - Using injections of 2 to 5 L, analyze each calibration standardaccording  to  Sec- tion 12 and tabulate peak height or area re- sponse against the concentration of 2,3,7,8– TCDD and internal standard. Calculate re- sponse factors (RF) for 2,3,7,8–TCDD using Equation  1.

As Cis 

## RF 

Ais Cs 

Equation   1

where:

As = SIM response for 2,3,7,8–TCDD m/z 320. Ais  = SIM response for the internal standard,

m/z 332 for 13 C12  2,3,7,8–TCDD m/z 328 for

37 Cl4  2,3,7,8–TCDD.

Cis  = Concentration of the internal standard (g/L).

Cs = Concentration of 2,3,7,8–TCDD (g/L).

If the RF value over the working range is a constant (<10% relative standard deviation, RSD), the RF can be assumed to be invariant and the average RF can be used for calcula- tions. Alternatively, the results can be used to plot a calibration curve of response ratios, As/Ais, vs. RF.

    - The working calibration curve or RF must be verified on each working day by the measurement of one or more 2,3,7,8–TCDD calibration standards. If the response for 2,3,7,8–TCDD varies from the predicted re- sponse by more than 15%, the test must be repeated using a fresh calibration standard. Alternatively, a new calibration  curve  must be prepared.

#### Pt. 136, App. A, Meth. 613

7.2 Before using any cleanup  procedure, the analyst must process a series of calibra- tion standards through the procedure to vali- date elution patterns and the absence of interferences from the reagents.

- Quality Control

  - Each laboratory that uses this method is required to operate a formal quality  con- trol program. The minimum requirements of this program consist of an initial demonstra- tion of laboratory capability and an ongoing analysis of spiked samples to evaluate and document data quality. The laboratory must maintain records to document the quality of data that is generated. Ongoing data quality checks are compared with established per- formance criteria to determine if the results of analyses meet the performance character- istics of the method. When results of sample spikes indicate atypical method perform- ance, a quality control check  standard  must be analyzed to confirm that the measure- ments were performed in an in-control mode of operation.

    - The analyst must make an initial, one-time, demonstration of the ability to generate acceptable accuracy and precision with this method. This  ability  is  established as described in Section 8.2.

    - In recognition of advances that are occurring in chromatography, the analyst is permitted certain options (detailed in Sec- tions 10.5, 11.1, and 12.1) to improve the sepa- rations or lower the cost of measurements. Each time such a modification is  made  to the method, the analyst is required to repeat the procedure in Section 8.2

    - Before processing any samples, the analyst must analyze a  reagent  water  blank to demonstrate that interferences from the analytical system and glassware are under control. Each time a set of samples is ex- tracted or reagents are changed, a reagent water blank must be processed as a safe- guard  against  laboratory  contamination.

    - The laboratory must, on an ongoing basis, spike and analyze a minimum of 10% of all samples with native 2,3,7,8–TCDD to monitor and evaluate laboratory data qual- ity. This procedure is described in Section 8.3.

    - The laboratory must, on an ongoing basis, demonstrate through the analyses of quality control  check standards  that  the op- eration of the measurement system is in con- trol.  This  procedure  is  described  in  Section

8.4. The frequency of the check standard analyses is equivalent to 10% of all samples analyzed but may be reduced if spike recov- eries from samples (Section 8.3) meet all specified quality control criteria.

    - The laboratory must maintain per- formance records to document the quality of data that is generated. This procedure is de- scribed in Section 8.5.

#### 40 CFR Ch. I (7–1–17 Edition)

  - To establish the ability to generate acceptable accuracy and precision, the ana- lyst must perform the following operations.

    - A quality control (QC) check sample concentrate is required containing 2,3,7,8– TCDD at a concentration of 0.100 g/mL in acetone. The  QC check  sample concentrate must be obtained from the U.S. Environ- mental Protection Agency, Environmental Monitoring and Support Laboratory in Cin- cinnati, Ohio, if available. If not available from that source, the QC check sample con- centrate must be obtained from another ex- ternal source. If not available from either source above, the QC check sample con- centrate must be prepared by the laboratory using stock standards prepared independ- ently from those used for calibration.

    - Using a pipet, prepare QC check sam- ples at a concentration of 0.100 g/L (100 ng/

L) by adding 1.00 mL of QC check sample concentrate to each of four 1–L aliquots of reagent water.

    - Analyze the well-mixed QC check samples according to the  method  beginning in Section 10.

    - Calculate the average recovery (X¯ ) in

g/L, and the standard deviation of the re- covery (s) in g/L, for 2,3,7,8–TCDD using the four  results.

    - Compare   s   and   (X¯ )   with   the   cor-

responding acceptance criteria for precision and accuracy, respectively, found in Table 2.

If s and X¯  meet the acceptance criteria, the

system performance is acceptable and anal- ysis of actual samples can begin. If s exceeds

the  precision  limit  or  X¯   falls  outside  the

range for accuracy,  the  system  performance is unacceptable for 2,3,7,8–TCDD. Locate and correct the source of the problem and repeat the test beginning with Section 8.2.2.

  - The laboratory must, on an ongoing basis, spike at least 10% of the samples from each sample site being monitored to assess accuracy. For laboratories analyzing one to ten samples per month, at least one spiked sample per month is required.

    - The concentration of the spike in the sample should be determined as follows:

      - If, as in compliance monitoring, the concentration of 2,3,7,8–TCDD in the sample is being checked against a regulatory concentration limit, the spike should be at that limit or 1 to 5 times higher than the background concentration determined in Section 8.3.2, whichever concentration would be larger.

      - If the concentration of 2,3,7,8–TCDD in the sample is not being checked against a limit specific to that parameter, the spike should be at 0.100 g/L or 1 to 5 times higher than the background concentration  deter- mined in Section 8.3.2, whichever concentra- tion would be larger.

      - If it is impractical to determine background levels before spiking (e.g., max- imum holding times will be exceeded), the

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 613

spike concentration should be (1) the regu- latory concentration limit, if any; or, if none

(2) the larger of either 5  times  higher  than the   expected   background   concentration   or

0.100 g/L.

    - Analyze one sample aliquot to deter- mine the background concentration (B) of 2,3,7,8–TCDD. If necessary, prepare a new QC check sample concentrate (Section 8.2.1) ap- propriate for the background concentration in the sample. Spike a second sample aliquot with 1.0 mL of the QC check sample con- centrate and analyze it to determine the concentration after spiking (A) of 2,3,7,8– TCDD. Calculate percent recovery (P) as 100(A¥B)%T, where T is the known true value of the spike.

    - Compare the percent recovery (P) for 2,3,7,8–TCDD with the corresponding QC ac- ceptance criteria found in Table 2. These ac- ceptance criteria were calculated to  include an allowance for error in measurement of both the background and spike concentra- tions, assuming a spike  to  background  ratio of 5:1. This error will be accounted for to the extent that the analyst’s spike to back- ground ratio approaches 5:1. 11 If spiking was performed   at   a   concentration   lower   than

0.100 g/L, the analyst must use  either  the QC acceptance criteria in Table 2, or op- tional QC acceptance criteria calculated for the specific spike concentration. To cal- culate optional acceptance criteria for the recovery of 2,3,7,8–TCDD: (1) Calculate accu- racy (X) using the equation in Table 3, sub- stituting  the  spike  concentration  (T)  for  C;

(2) calculate overall precision (S) using the equation in Table 3, substituting Xfor X; (3) calculate the range for recovery at the spike concentration as (100 X/T)2.44(100 S/T)%. 11

8.3.4 If the recovery of 2,3,7,8–TCDD falls outside the designated range for recovery, a check standard must be analyzed as de- scribed in Section 8.4.

  - If the recovery of 2,3,7,8–TCDD fails the acceptance criteria for recovery in Sec- tion 8.3, a QC check standard must be pre- pared and analyzed.

NOTE: The frequency for the required anal- ysis of a QC check standard will depend upon the complexity of the sample matrix and the performance of the laboratory.

    - Prepare the QC check standard by adding 1.0 mL of QC check sample con- centrate (Section 8.2.1 or 8.3.2) to 1 L of rea- gent water.

    - Analyze the QC check standard to determine the concentration measured (A) of 2,3,7,8–TCDD. Calculate the percent recovery (Ps) as 100 (A/T)%, where T is the true value of the standard concentration.

    - Compare the percent recovery (Ps) with the corresponding QC acceptance cri- teria found in Table 2. If the recovery of 2,3,7,8–TCDD falls outside the designated range, the laboratory performance  is  judged to  be  out  of  control,  and  the  problem  must

be immediately identified and corrected. The analytical result for 2,3,7,8–TCDD in the unspiked sample is suspect and may not be reported for regulatory compliance purposes.

  - As part of the QC program for the lab- oratory, method accuracy for wastewater samples must be assessed and records must be maintained. After the analysis of five spiked wastewater samples as in Section 8.3,

calculate  the  average  percent  recovery  (P¯ )

and the spandard deviation of the percent re- covery (sp). Express the accuracy assessment

as a percent recovery interval from P¯ ¥2sp to P¯ + 2sp. If P¯ = 90% and sp = 10%, for example,

the accuracy interval is expressed as 70– 110%. Update the accuracy assessment on a regular basis (e.g. after each five to ten new accuracy    measurements).

  - It is recommended that the laboratory adopt additional quality assurance practices for use  with  this method.  The  specific  prac- tices that  are  most  productive  depend  upon the needs of the laboratory and the nature of the samples. Field duplicates may be ana- lyzed to assess the precision of the environ- mental measurements. Whenever  possible, the laboratory should analyze standard ref- erence materials and participate in relevant performance evaluation studies.

- Sample Collection, Preservation, and Handling

  - Grab samples must be collected  in glass containers. Conventional sampling practices 12 should be followed, except that the bottle must not be prerinsed with sample before collection. Composite samples should be collected in refrigerated  glass  containers in accordance with the requirements of the program. Automatic sampling equipment must be as free as possible of Tygon tubing and other potential sources of contamina- tion.

  - All samples must be iced or refrig- erated at 4 C and protected from light from the time of collection until extraction.  Fill the sample bottles and, if residual chlorine is present, add 80 mg of sodium thiosulfate per liter of sample and mix well. EPA Methods

330.4 and 330.5 may be used for measurement of residual chlorine. 13 Field test kits are available for this purpose.

  - Label all samples and containers ‘‘POISON’’ and ship according to applicable

U.S. Department of Transportation regula- tions.

  - All samples must be extracted within 7 days of collection and completely analyzed within 40 days of extraction. 2

- Sample Extraction

CAUTION: When using this method to ana- lyze for 2,3,7,8–TCDD, all of the following op- erations must be performed in a limited-ac- cess laboratory with the analyst wearing full

#### Pt. 136, App. A, Meth. 613

protective covering for all exposed skin sur- faces. See Section 4.2.

  - Mark the water meniscus on the side of the sample bottle for later determination of sample volume. Pour the entire sample into a 2–L separatory funnel.

  - Add 1.00 mL of  internal  standard spiking solution to the sample in the sepa- ratory funnel. If the final extract will be concentrated  to  a  fixed  volume  below   1.00 mL (Section 12.3), only that volume  of  spik- ing solution should be added to the sample so that the final  extract  will  contain  25  ng/mL of  internal  standard  at  the  time  of  analysis.

  - Add 60 mL of methylene chloride  to the sample bottle, seal, and shake 30 s to rinse the inner surface. Transfer the solvent to the separatory funnel and extract the sample by shaking the funnel for 2 min. with periodic venting to release excess pressure. Allow the organic layer to separate from the water phase for a minimum of 10 min. If the emulsion interface between layers is more than one-third the vmlume of the solvent layer, the analyst must employ mechanical techniques to complete the phase separation. The optimum technique depends upon the sample, but may include  stirring,  filtration of the emulsion through glass wool, cen- trifugation, or other physical methods. Col- lect the methylene chloride extract in a 250- mL  Erlenmeyer  flask.

  - Add a second 60-mL volume of meth- ylene chloride to the sample bottle and re- peat the extraction procedure a second time, combining the extracts in the Erlenmeyer flask. Perform a third extraction in the same manner.

  - Assemble a Kuderna-Danish (K-D) concentrator by attaching a 10-mL concen- trator tube to a 500-mL evaporative flask. Other concentration devices or  techniques may be used in place of the K-D concentrator if the requirements of Section 8.2 are met.

  - Pour the combined extract into the K-D  concentrator.  Rinse  the  Erlenmeyer flask with 20 to 30 mL of methylele chloride to complete the quantitative transfer.

  - Add one or two clean boiling chips to the evaporative flask and attach a three-ball Snyder column. Prewet the Snyder  column by adding about 1 mL of methylene chloride to the top. Place the K-D apparatus on a hot water bath (60 to 65 C) so that the concen- trator tube is partially immersed in the hot water, and the entire lower rounded surface of the flask is bathed with hot vapor. Adjust the vertical position of the apparatus  and the water temperature as required to com- plete the concentration in 15 to  20  min.  At the proper rate of distillation the balls of the column will actively chatter but the cham- bers will not flood with condensed solvent. When the apparent volume of liquid reaches 1 mL, remove the K-D apparatus and allow it to drain and cool for at least 10 min.

#### 40 CFR Ch. I (7–1–17 Edition)

  - Momentarily remove the Snyder col- umn, add 50 mL of hexane and a new boiling chip, and reattach the Snyder column.  Raise the temperature of the water bath to 85 to 90

C. Concentrate the  extract  as  in  Section 10.7, except use hexane to prewet the column. Remove the Snyder column and rinse the flask and its lower joint into the concen- trator tube with 1 to 2 mL of hexane. A 5-mL syringe is recommended for this operation. Set aside the K-D glassware for reuse in Sec- tion 10.14.

  - Pour the hexane extract from the concentrator tube into a 125-mL separatory funnel. Rinse the concentrator tube four times with 10-mL aliquots of hexane. Com- bine all rinses in the 125-mL separatory fun- nel.

  - Add 50 mL of sodium hydroxide solu- tion to the funnel and shake for 30 to 60 s. Discard the aqueous phase.

  - Perform a second wash of the or- ganic layer with 50 mL of reagent water. Dis- card the aqueous phase.

  - Wash the hexane layer with a least two 50-mL aliquots of concentrated sulfuric acid. Continue washing the  hexane  layer with 50-mL aliquots of concentrated sulfuric acid until the acid layer remains colorless. Discard  all  acid  fractions.

  - Wash the hexane layer with two 50- mL aliquots of reagent water. Discard the aqueous phases.

  - Transfer the hexane extract into a 125-mL Erlenmeyer flask containing 1 to 2 g of anhydrous sodium sulfate. Swirl the flask for 30  s and  decant  the hexane  extract into the reassembled  K-D  apparatus.  Complete the quantitative transfer with two 10-mL hexane rinses of the Erlenmeyer flask.

  - Replace the one or two clean boiling chips and concentrate the extract to  6  to  10 mL as in Section 10.8.

  - Add a clean boiling chip to the con- centrator tube and attach a two-ball micro- Snyder column. Prewet the column by  add- ing about 1 mL of hexane  to  the  top.  Place the micro-K-D apparatus on  the  water  bath so that the concentrator tube is partially immersed in the hot water. Adjust the vertical position of the apparatus and the water temperature as required to complete the concentration in 5 to 10 min. At the prop- er rate of distillation the balls of the column will actively chatter but the chambers will not flood. When the apparent volume of liq- uid reaches about 0.5 mL, remove the K-D apparatus and allow it to drain and cool for at least 10 min. Remove the micro-Snyder column and rinse its lower joint into the concentrator tube with 0.2 mL of hexane.

Adjust the extract volume to 1.0 mL with hexane. Stopper the concentrator tube and store refrigerated and protected from light if further processing will not be performed im- mediately.   If   the   extract   will   be   stored

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 613

longer than two days, it should be trans- ferred to a Teflon-sealed screw-cap vial.  If the sample extract requires no further clean- up, proceed  with  GC/MS  analysis  (Section 12). If the sample requires further cleanup, proceed to Section 11.

  - Determine the original sample vol- ume by refilling the sample bottle to the mark and transferring the liquid to  a  1000- mL graduated cylinder. Record the sample volume to the nearest 5 mL.

- Cleanup and Separation

  - Cleanup procedures may not be nec- essary for a relatively clean sample matrix. If particular circumstances demand the use of a cleanup procedure, the analyst may use either procedure below or any other appro- priate procedure. 1 5M7 However, the analyst first  must  demonstrate  that  the  require- ments of Section 8.2 can be met using the method as revised to incorporate the cleanup procedure. Two cleanup column options are offered  to  the  analyst  in  this  section.  The alumina column should be used first to over- come interferences. If background problems are still encountered, the silica gel column may be helpful.

  - Alumina column cleanup for 2,3,7,8– TCDD:

    - Fill a 300 mm long 10 mm ID chromatographic column with activated alu- mina to the 150 mm level. Tap the column gently to settle the alumina and add 10 mm of anhydrous sodium sulfate to the top.

    - Preelute the column with 50 mL of hexane. Adjust the elution rate to 1 mL/min. Discard the eluate and just prior to exposure of the sodium sulfate layer to the air, quan- titatively transfer the 1.0-mL sample extract onto the column using two 2-mL portions of hexane to complete the transfer.

    - Just prior to exposure of the sodium sulfate layer to the air, add 50 mL of 3% methylene chloride/95% hexane (V/V) and continue the elution of the column.  Discard the  eluate.

    - Next, elute the column  with  50  mL of 20% methylene chloride/80% hexane (V/V) into a 500-mL K-D flask equipped  with  a  10- mL concentrator tube. Concentrate the col- lected fraction to 1.0 mL as in  Section  10.16 and analyze by GC/MS (Section 12).

  - Silica gel column cleanup for 2,3,7,8– TCDD:

    - Fill a 400 mm long 11 mm ID chromatmgraphic column with silica gel to the 300 mm level. Tap the column gently to settle the silica gel and add 10 mm of anhy- drous sodium sulfate to the top.

    - Preelute the  column with  50 mL  of 20% benzene/80% hexane (V/V). Adjust the elution rate to 1 mL/min. Discard the eluate and just prior to exposure of the sodium sul- fate layer to the air, quantitatively  transfer the  1.0-mL  sample  extract  onto  the  column

using two 2-mL portions of 20% benzene/80% hexane  to  complete  the  transfer.

    - Just prior to  exposure of  the sodium sulfate layer to the air, add 40 mL of 20% benzene/80% hexane to the column. Collect the eluate in a  clean  500-mL  K-D  flask equipped with a 10-mL concentrator tube. Concentrate the collected fraction  to  1.0  mL as in Section 10.16 and analyze by GC/MS.

- GC/MS Analysis

12.1 Table 1 summarizes the recommended operating conditions for the gas chro- matograph. Included in this table are reten- tion times and MDL that  can  be  achieved under these conditions. Other capillary col- umns or chromatographic conditions may be used if the requirements of Sections 5.5.2 and

8.2 are met.

  - Analyze standards  and  samples  with the mass spectrometer operating in the se- lected ion monitoring (SIM) mode  using  a dwell time to give at least seven points per peak. For LRMS, use masses at m/z 320, 322, and 257 for 2,3,7,8–TCDD and either m/z 328 for 37Cl4 2,3,7,8–TCDD or m/z 332 for 13C12 2,3,7,8–TCDD. For HRMS, use masses at m/z 319.8965 and 321.8936 for 2,3,7,8–TCDD and ei- ther m/z 327.8847 for 37Cl4 2,3,7,8–TCDD or m/ z 331.9367 for 13C12 2,3,7,8–TCDD.

  - If lower detection limits are required, the extract may be carefully evaporated to dryness under a gentle stream of nitrogen with the concentrator tube  in  a  water  bath at about 40 C. Conduct this operation imme- diately before  GC/MS  analysis.  Redissolve the extract in the desired final volume of ortho-xylene or tetradecane.

  - Calibrate the system daily as de- scribed in Section 7.

  - Inject 2 to 5 L of the sample extract into the gas chromatograph. The volume of calibration standard injected must be meas- ured, or be the same as all sample injection volumes.

  - The presence of 2,3,7,8–TCDD is quali- tatively confirmed if all of the following cri- teria are achieved:

    - The gas chromatographic column must resolve 2,3,7,8–TCDD from the other 21 TCDD  isomers.

    - The masses for native 2,3,7,8–TCDD (LRMS-m/z 320, 322, and 257 and HRMS-m/z 320 and 322) and labeled 2,3,7,8–TCDD (m/z 328 or 332) must exhibit a  simultaneous  max- imum at a  retention  time  that  matches  that of native 2,3,7,8–TCDD in the calibration standard,  with  the  performance  specifica- tions  of  the  analytical  system.

    - The chlorine isotope ratio at m/z 320 and m/z 322 must agree to within10% of that in  the  calibration  standard.

    - The signal of all peaks must be greater than 2.5 times the noise level.

  - For quantitation, measure the re- sponse of the m/z 320 peak for 2,3,7,8–TCDD

#### Pt. 136, App. A, Meth. 613

and the m/z 332 peak for 13C12 2,3,7,8–TCDD or the m/z 328 peak for 37Cl4 2,3,7,8–TCDD.

  - Co-eluting impurities are suspected if all criteria are achieved except those in Sec- tion 12.6.3. In this case, another SIM analysis using masses at m/z 257, 259, 320 and either m/ a 328 or m/z 322 can be performed. The masses at m/z 257 and m/z 259 are indicative of the loss of one chlorine and one carbonyl group from 2,3,7,8–TCDD. If masses m/z 257 and m/z 259 give a chlorine isotope ratio that agrees to within 10% of the same cluster in the calibration standards, then the presence of TCDD can be confirmed.  Co-eluting  DDD, DDE, and PCB residues can be confirmed, but will require another injection using the appropriate SIM masses or full  repetitive mass scans. If the response for 37Cl4 2,3,7,8– TCDD at m/z 328 is too large, PCB contami- nation is suspected and can be confirmed by examining the response at both m/z 326 and m/z 328. The 37Cl4 2,3,7,8–TCDD internal standard gives negligible response at m/z 326. These pesticide residues can be removed using the alumina column cleanup  proce- dure.

  - If broad background interference re- stricts the sensitivity of the GC/MS analysis, the analyst should employ additional  clean- up procedures and reanalyze by GC/MS.

  - In those circumstances where these procedures do not yield a definitive conclu- sion, the use of high resolution mass spec- trometry is suggested. 5

- Calculations

  - Calculate the concentration of 2,3,7,8– TCDD in the sample using the response fac- tor (RF) determined in Section 7.1.2 and Equation 2.

AVt 

## Concentration (g/L) 

Vi Vs 

Equation   2

where:

As   =  SIM  response  for  2,3,7,8–TCDD  at  m/z 320.

Ais   =  SIM  response  for  the  internal  standard at m/z 328 or 332.

Is   =  Amount  of  internal  standard  added  to each extract (g).

Vo = Volume of water extracted (L).

  - For each sample, calculate the per- cent recovery of the internal standard by comparing the area of the m/z peak measured in the sample to the area of the same peak in the calibration standard. If the recovery is below 50%, the analyst should review all as- pects of his analytical technique.

  - Report results in g/L without correc- tion for recovery data. All QC data obtained should be reported with the sample results.

#### 40 CFR Ch. I (7–1–17 Edition)

- Method Performance

  - The method detection limit (MDL) is defined as the minimum concentration of a substance that can be measured and reported with 99% confidence that the value is above zero. 1  The  MDL  concentration  listed   in Table 1 was obtained using reagent water. 14 The MDL actually achieved in a given  anal- ysis will vary depending on instrument sen- sitivity  and  matrix  effects.

  - This method was tested by 11 labora- tories using reagent water, drinking water, surface water, and three industrial wastewaters  spiked  at  six  concentrations over the range 0.02 to 0.20 g/L. 15 Single oper- ator precision, overall precision, and method accuracy were found to be directly  related  to the concentration of the parameter and es- sentially independent of the sample matrix. Linear equations to describe these relation- ships are presented in Table 3.

REFERENCES

- 40 CFR part 136, appendix B.

- ‘‘Determination  of  TCDD   in   Industrial and Municipal Wastewaters,’’ EPA 600/4–82– 028, National Technical Information Service, PB82–196882, Springfield, Virginia 22161, April 1982.

- Buser, H.R., and Rappe, C. ‘‘High Resolu- tion Gas Chromatography of the 22 Tetrachlorodibenzo-p-dioxin Isomers,’’ Ana- lytical Chemistry, 52, 2257 (1980).

- ASTM Annual Book of Standards, Part 31, D3694–78. ‘‘Standard Practices for Prepa- ration of Sample Containers and for Preser- vation of Organic Constituents,’’ American Society for Testing and Materials, Philadel- phia.

- Harless, R. L., Oswald, E. O., and Wilkinson, M. K. ‘‘Sample Preparation and Gas Chromatography/Mass Spectrometry De- termination of 2,3,7,8-Tetrachlorodibenzo-p- dioxin,’’ Analytical Chemistry, 52, 1239 (1980).

- Lamparski, L. L., and Nestrick, T. J. ‘‘Determination of Tetra-, Hepta-, and Octachlorodibenzo-p-dioxin Isomers in Par- ticulate Samples at Parts per Trillion Lev- els,’’ Analytical Chemistry, 52, 2045 (1980).

- Longhorst, M. L., and Shadoff, L. A. ‘‘Determination of Parts-per-Trillion Con- centrations of Tetra-, Hexa-, and Octachlorodibenzo-p-dioxins in Human Milk,’’ Analytical Chemistry, 52, 2037 (1980).

- ‘‘Carcinogens—Working with Carcino- gens,’’ Department of Health, Education, and Welfare, Public Health Service, Center for Disease Control, National Institute for Occu- pational Safety and Health, Publication No. 77–206, August 1977.

- ‘‘OSHA Safety and Health Standards, General Industry,’’ (29 CFR part 1910), Occuptional Safety and Health Administra- tion, OSHA 2206 (Revised, January 1976).

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 624

- ‘‘Safety in Academic Chemistry Labora- tories,’’ American Chemical Society Publica- tion, Committee on Chemical Safety, 3rd Edition, 1979.

- Provost,  L. P., and  Elder,  R. S., ‘‘Inter- pretation  of  Percent  Recovery  Data,’’  Amer- ican Laboratory, 15, 58–63 (1983). (The value

2.44 used in the equation in Section 8.3.3 is two times the value 1.22 derived in this re- port.)

- ASTM Annual Book of Standards, Part 31, D3370–76, ‘‘Standard Practices for Sam- pling Water,’’ American Society for Testing and  Materials,  Philadelphia.

- ‘‘Methods, 330.4 (Titrimetric, DPD-FAS) and 330.5 (Spectrophotometric DPD) for Chlorine, Total Residual,’’ Methods for Chemical Analysis of Water and Wastes, EPA–600/4–79–020, U.S. Environmental Pro- tection Agency, Environmental Monitoring and Support Laboratory, Cincinnati, Ohio 45268, March 1979.

- Wong, A.S. et al.  ‘‘The  Determination of 2,3,7,8–TCDD in Industrial and Municipal Wastewaters, Method 613, Part 1—Develop- ment  and  Detection  Limits,’’  G.  Choudhay,

L.  Keith,  and  C.  Ruppe,  ed.,  Butterworth Inc., (1983).

- ‘‘EPA Method Study 26, Method 613: 2,3,7,8–Tetrachlorodibenzo-p-dioxin,’’ EPA 600/4–84–037, National Technical Information

Service,    PB84–188879,     Springfield,    Virginia 22161, May 1984.

TABLE 1—CHROMATOGRAPHIC CONDITIONS AND

METHOD DETECTION LIMIT

| Parameter | Retention time (min) | Method detection limit (g/ L) |
| --- | --- | --- |
| 2,3,7,8–TCDD .................................... | 13.1 | 0.002 |

Column conditions: SP–2330 coated on a 60 m long 0.25 mm ID glass column with hydrogen carrier gas at 40 cm/sec linear velocity, splitless injection using tetradecane. Column temperature held isothermal at 200 C for 1 min, then pro- grammed at 8 C/min to 250 C and held. Use of helium car- rier gas will approximately double the retention time.

TABLE 2—QC ACCEPTANCE CRITERIA—METHOD 613

| Parameter | Test conc. (g/L) | Limit for s (g/L) | Range for X (g/L) | Range for P, Ps (%) |
| --- | --- | --- | --- | --- |
| 2,3,7,8–TCDD | 0.100 | 0.0276 | 0.0523–0.1226 | 45–129 |

s = Standard deviation of four recovery measurements, in

g/L (Section 8.2.4).

X¯  = Average recovery for four recovery measurements, in

g/L (Section 8.2.4).

P, Ps = Percent recovery measured (Section 8.3.2, Section 8.4.2).

NOTE: These criteria are based directly upon the method performance data in Table 3. Where necessary, the limits for recovery have been broadened to assure applicability of the limits to concentrations below those used to develop Table 3.

TABLE 3—METHOD ACCURACY AND PRECISION AS FUNCTIONS OF CONCENTRATION—METHOD 613

| Parameter | Accuracy, as recov- ery, X(g/L) | Single analyst, pre- cision, sr(/L) | Overall precision, S(/g/L) |
| --- | --- | --- | --- |
| 2,3,7,8-TCDD ............................................................................ | 0.86C + 0.00145 | 0.13X¯ + 0.00129 | 0.19X¯ + 0.00028 |

X= Expected recovery for one or more measurements. of a sample containing a concentration of C, in g/L.

sr= Expected single analyst standard deviation of measurements at an average concentration found of X¯ , in g/L. S= Expected interlaboratory standard deviation of measurements at an average concentration found of X¯ , in g/L. C = True value for the concentration, in g/L.

X¯ = Average recovery found for measurements of samples containing a concentration of C, in g/L.

| Parameter | STORET No. | CAS No. |
| --- | --- | --- |
| 1,3-Dichlorobenzene ....................... | 34566 | 541–73–1 |
| 1,4-Dichlorobenzene ....................... | 34571 | 106–46–7 |
| 1,1-Dichloroethane .......................... | 34496 | 75–34–3 |
| 1,2-Dichloroethane .......................... | 34531 | 107–06–2 |
| 1,1-Dichloroethane .......................... | 34501 | 75–35–4 |
| trans-1,2-Dichloroethene ................. | 34546 | 156–60–5 |
| 1,2-Dichloropropane ........................ | 34541 | 78–87–5 |
| cis-1,3-Dichloropropene .................. | 34704 | 10061–01–5 |
| trans-1,3-Dichloropropene .............. | 34699 | 10061–02–6 |
| Ethyl benzene ................................. | 34371 | 100–41–4 |
| Methylene chloride .......................... | 34423 | 75–09–2 |
| 1,1,2,2-Tetrachloroethane ............... | 34516 | 79–34–5 |
| Tetrachloroethene ........................... | 34475 | 127–18–4 |
| Toluene ........................................... | 34010 | 108–88–3 |
| 1,1,1-Trichloroethene ...................... | 34506 | 71–55–6 |
| 1,1,2-Trichloroethene ...................... | 34511 | 79–00–5 |
| Trichloroethane ............................... | 39180 | 79–01–6 |
| Trichlorofluoromethane ................... | 34488 | 75–69–4 |
| Vinyl chloride ................................... | 39175 | 75–01–4 |

METHOD 624—PURGEABLES

  - Scope and Application

  - This method covers the determination of a number of purgeable organics. The fol- lowing parameters may be determined by this method:

| Parameter | STORET No. | CAS No. |
| --- | --- | --- |
| Benzene .......................................... | 34030 | 71–43–2 |
| Bromodichloromethane ................... | 32101 | 75–27–4 |
| Bromoform ...................................... | 32104 | 75–25–2 |
| Bromomethane ................................ | 34413 | 74–83–9 |
| Carbon tetrachloride ....................... | 32102 | 56–23–5 |
| Chlorobenzene ................................ | 34301 | 108–90–7 |
| Chloroethane ................................... | 34311 | 75–00–3 |
| 2-Chloroethylvinyl ether .................. | 34576 | 110–75–8 |
| Chloroform ...................................... | 32106 | 67–66–3 |
| Chloromethane ................................ | 34418 | 74–87–3 |
| Dibromochloromethane ................... | 32105 | 124–48–1 |
| 1,2-Dichlorobenzene ....................... | 34536 | 95–50–1 |

#### Pt. 136, App. A, Meth. 624

  - The method may be extended to screen samples for acrolein (STORET No. 34210, CAS No. 107–02–8) and acrylonitrile (STORET No. 34215, CAS No. 107–13–1), however, the pre- ferred method for these two compounds in Method 603.

  - This is a purge and trap gas chromatographic/mass spectrometer (GC/MS) method  applicable  to  the  determination  of the compounds listed above in municipal and industrial discharges as  provided  under  40 CFR 136.1.

  - The method detection limit (MDL, de- fined in Section 14.1) 1 for each parameter is listed in Table 1. The MDL for a specific wastewater may differ from those listed, de- pending upon the nature of interferences  in the sample matrix.

  - Any modification to this method, be- yond those expressly permitted, shall be con- sidered as a major modification subject to application and approval of alternate test procedures under 40 CFR 136.4 and 136.5. De- pending upon the nature of the modification and the extent of intended use, the applicant may be required to demonstrate that the modifications will produce equivalent results when applied to relevant wastewaters.

  - This method is restricted to use by or under the supervision of analysts experi- enced in the operation of a purge and trap system and a gas chromatograph/mass spec- trometer and in the interpretation of mass spectra. Each analyst must demonstrate the ability to generate acceptable results with this method using the procedure described in Section 8.2.

  - Summary of Method

2.1 An inert gas is bubbled through a 5-mL water sample contained in a specially-de- signed purging chamber at ambient tempera- ture. The purgeables are efficiently trans- ferred from the aqueous phase to the vapor phase. The vapor is swept through a sorbent trap where the purgeables are trapped. After purging is completed, the trap is heated and backflushed with the inert gas to desorb the purgeables onto a gas chromatographic col- umn. The gas chromatograph is temperature programmed to separate the purgeables which are then detected with a mass spec- trometer. 2 3

  - Interferences

  - Impurities in the purge gas, organic compounds outgassing from the plumbing ahead of the trap, and solvent vapors in the laboratory account for the majority of con- tamination problems. The analytical system must be demonstated to be free from con- tamination under the conditions of the anal- ysis by running laboratory reagent blanks as described in Section 8.1.3. The use of non- Teflon plastic tubing, non-Teflon thread sealants,   or   flow   controllers   with   rubber

#### 40 CFR Ch. I (7–1–17 Edition)

components in the purge and trap system should be avoided.

  - Samples can be contaminated by diffu- sion of volatile organics (particularly fluoro- carbons and methylene chloride) through the septum seal into the sample during shipment and storage. A field reagent blank prepared from reagent water and carried through the sampling and handling protocol can serve as a check on such contamination.

  - Contamination by  carry-over  can occur whenever high level and low level sam- ples are sequentially analyzed. To reduce carry-over, the purging device and sample syringe must be rinsed with reagent water between sample analyses. Whenever an un- usually concentrated sample  is  encountered, it should be followed by an analysis of rea- gent water to check for cross contamination. For samples containing large amounts of water-soluble materials, suspended solids, high boiling compounds or high pureeable levels, it may be necessary to wash the purg- ing device with a detergent solution, rinse it with distilled water, and then dry it in a 105

C oven between analyses. The trap and other parts of the system are also subject to contamination; therefore, frequent bakeout and purging of the entire system may be re- quired.

  - Safety

4.1   The   toxicity   or   carcinogenicity   of each  reagent  used  in  this  method  has  not been precisely defined; however, each chem- ical compound should be treated as a poten- tial health hazard. From this viewpoint, ex- posure to these chemicals must be reduced to the lowest possible level by whatever means available. The laboratory is responsible for maintaining   a   current   awareness   file   of OSHA  regulations  regarding  the  safe  han- dling   of   the   chemicals   specified   in   this methmd.  A  reference  file  of  material  data handling sheets should also be made avail- able to all personnel involved in the chem- ical  analysis.  Additional  references  to  lab- oratory safety are available and have been identified 4M6  for the information of the an- alyst.

4.2. The following parameters covered by this method have been  tentatively  classified as known or suspected, human or mamma- lian carcinogens: benzene, carbon tetra- chloride, chloroform, 1,4-dichlorobenzene, and vinyl chloride. Primary standards of these toxic compounds should be prepared in a hood. A NIOSH/MESA approved toxic gas respirator should be worn when the analyst handles high concentrations of these toxic compounds.

  - Apparatus and Materials

  - Sampling equipment, for discrete sam- pling.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 624

    - Vial—25-mL capacity or larger, equipped with a screw cap with a hole in the center (Pierce #13075 or equivalent). Deter- gent wash, rinse with tap and distilled  water, and dry at 105 C before use.

    - Septum—Teflon-faced	silicane (Pierce #12722 or equivalent). Detergent wash, rinse with tap and distilled water, and dry at 105 C for 1 h before use.

  - Purge and trap system—The purge and trap system consists of three separate pieces of equipment: A purging device, trap, and desorber. Several complete systems are now commercially available.

    - The purging device must be designed to accept 5-mL samples with a water column at least 3 cm deep. The gaseous head space between the water column and the trap must have a total volume of less than 15 mL. The purge gas must pass though the water col- umn as finely divided bubbles with a diame- ter of less than 3 mm at the origin. The purge gas must be introduced no more than

5 mm from the base of the water  column. The purging device illustrated in Figure 1 meets these design criteria.

    - The trap must be at least 25 cm long and have an inside diameter of at least 0.105 in. The trap must be packed to contain the following minimum lengths of adsorbents: 1.0 cm of methyl silicone coated packing (Sec- tion 6.3.2), 15 cm of 2,6-dyphenylene oxide polymer (Section 6.3.1), and 8 cm of silica gel (Section 6.3.3). The minimum specifications for the trap are illustrated in Figure 2.

    - The desorber should be capable of rapidly heating the trap to 180 C. The poly- mer section of the trap should not be heated higher than 180 C and the remaining sec- tions should not exceed 200 C. The desorber illustrated in Figure 2 meets these design criteria.

    - The purge and trap system may be assembled as a separate unit or be coupled to a gas chromatograph as illustrated in Fig- ures 3 and 4.

  - GC/MS system:

    - Gas chromatograph—An analytical system complete  with  a  temperature  pro- grammable gas chromatograph suitable for on-column injection and all required acces- sories including syringes, analytical  col- umns, and gases.

    - Column—6 ft long 0.1 in ID stain- less steel or glass, packed with 1% SP–1000 on Carbopack B (60/80 mesh) or equivalent. This column was used to develop the method performance statements in Section 14. Guidelines for the use of alternate column packings are provided in Section 11.1.

    - Mass spectrometer—Capable of scan- ning from 20 to 260 amu every 7 s or less, uti- lizing 70 V (nominal) electron energy in the electron impact ionization mode, and pro- ducing a mass spectrum which meets all the criteria   in   Table   2   when   50   ng   of   4-

bromofluorobenzene	(BFB)	is	injected through the  GC  inlet.

    - GC/MS interface—Any GC to MS interface that gives acceptable calibration points at 50 ng or less per injection for each of the parameters of interest and achieves all acceptable performance criteria (Section 10) may be used. GC to MS interfaces con- structed of all glass or glass-lined  materials are recommended. Glass can be  deactivated by  silanizing  with  dichlorodimethylsilane.

    - Data system—A computer system must be interfaced to the mass spectrometer that allows the continuous acquisition and storage on machine-readable media of  all mass spectra obtained throughout the dura- tion of the chromatographic program. The computer must have software that allows searching any GC/MS data file for specific m/ z (masses) and plotting such m/z abundances versus time or scan number. This type of plot is defined as an Extracted Ion Current Profile (EICP). Software must also be avail- able that allows integrating  the  abundance in any EICP between specified time or scan number  limits.

  - Syringes—5-mL,  glass  hypodermic with Luerlok tip (two each), if applicable to the purging device.

  - Micro syringes—25-L, 0.006 in. ID nee-

dle.

  - Syringe valve—2-way, with Luer ends (three each).

  - Syringe—5-mL, gas-tight with shut-off valve.

  - Bottle—15-mL, screw-cap, with Teflon cap liner.

  - Balance—Analytical, capable of accu- rately weighing 0.0001 g.

  - Reagents

  - Reagent water—Reagent water is de- fined as a water in which an  interferent  is not observed at the  MDL  of  the  parameters of  interest.

    - Reagent water can be generated by passing tap water through a carbon filter bed containing about 1 lb of activated carbon (Filtrasorb–300, Calgon Corp., or equivalent).

    - A water  purification  system (Millipore Super-Q or equivalent)  may  be used to generate reagent water.

    - Reagent water may also be prepared by boiling water for 15 min. Subsequently, while maintaining the temperature at 90 C, bubble a contaminant-free inert gas through the water for 1 h. While  still  hot,  transfer the water to a narrow mouth screw-cap bot- tle and  seal with  a  Teflon-lined septum  and cap.

  - Sodium thiosulfate—(ACS) Granular.

  - Trap materials:

    - 2,6-Diphenylene oxide polymer— Tenax, (60/80 mesh), chromatographic  grade or   equivalent.

    - Methyl silicone packing—3% OV–1 on Chromosorb-W (60/80 mesh) or equivalent.

#### Pt. 136, App. A, Meth. 624

    - Silica gel—35/60 mesh, Davison, grade-15 or equivalent.

  - Methanol—Pesticide quality or equiv- alent.

  - Stock standard solutions—Stock standard solutions may be prepared from pure standard materials or purchased as cer- tified solutions. Prepare stock standard solu- tions in methanol using assayed liquids or gases as appropriate. Because of the toxicity of some of the compounds, primary dilutions of these materials should be prepared in a hood. A NIOSH/MESA approved toxic gas respirator should be used when the analyst handles high concentrations of such mate- rials.

    - Place about  9.8  mL  of  methanol  into a 10-mL ground glass stoppered volumetric flask. Allow the flask to stand,  unstoppered, for about 10 min or until all alcohol wetted surfaces have dried. Weigh the flask to the nearest 0.1 mg.

    - Add the assayed reference material:

      - Liquids—Using a 100-L syringe, immediately add two or more drops of as- sayed reference material to the flask, then reweigh. Be sure that the drops fall directly into the alcohol without contacting the neck of the flask.

      - Gases—To prepare standards for any  of  the  four  halocarbons  that  boil  below

30 C (bromomethane, chloroethane, chloromethane, and vinyl chloride), fill a  5- mL valved gas-tight syringe with the ref- erence standard to the 5.0-mL mark.  Lower the needle to 5 mm above the methanol me- niscus. Slowly introduce the reference stand- ard above the surface of the liquid (the heavy gas will rapidly dissolve in the methanol).

    - Reweigh, dilute to volume, stopper, then mix by inverting the flask  several times. Calculate the concentration in g/L from the net gain in weight. When compound purity is assayed to be 96% or greater, the weight may be used without correction to calculate the concentration of the stock standard. Commercially prepared stock standards may be used at any concentration if they are certified by the manufacturer or by an independent source.

    - Transfer the stock standard solution into a Teflon-sealed screw-cap bottle. Store, with minimal headspace, at ¥10 to ¥20 C and protect from light.

    - Prepare fresh standards weekly for the four gases and 2-chloroethylvinyl ether. All other standards must be replaced after one month, or sooner if comparison with check standards indicates a problem.

  - Secondary dilution standards—Using stock solutions, prepare secondary dilution standards in methanol that contain the com- pounds of interest, either singly or mixed to- gether. The secondary dilution standards should be prepared at concentrations such that the aqueous calibration standards pre- pared in Section 7.3 will bracket the working

#### 40 CFR Ch. I (7–1–17 Edition)

range of the analytical system. Secondary dilution standards should be stored with minimal headspace and should be checked frequently for signs of degradation or evapo- ration, especially just prior to preparing calibration standards from them.

  - Surrogate standard spiking solution— Select a minimum of three surrogate com- pounds from Table 3. Prepare stock standard solutions for each surrogate standard in methanol as described in Section 6.5. Prepare a surrogate standard spiking solution from these stock standards at a  concentration  of 15 g/mL in water. Store the solutions at 4 C in Teflon-sealed glass containers with a min- imum of headspace. The solutions should be checked frequently for stability. The addi- tion of 10 L of this solution of 5 mL of sam- ple or standard is equivalent to a concentra- tion of 30 g/L of each surrogate standard.

  - BFB Standard—Prepare a 25 g/mL so- lution of BFB in methanol.

  - Quality control check sample con- centrate—See Section 8.2.1.

  - Calibration

  - Assemble a purge and trap system that meets the  specifications in  Section 5.2.  Con- dition the trap overnight at 180 C by backflushing with an inert gas flow of at least 20 mL/min. Condition the trap for 10 min once daily prior to use.

  - Connect the purge and trap system to a gas chromatograph. The gas chro- matograph must be operated using tempera- ture and flow rate conditions equivalent to those given in Table 1.

  - Internal standard calibration proce- dure—To use this approach, the analyst must select three or more internal standards that are similar in analytical behavior to the compounds of interest. The analyst must fur- ther demonstrate that the measurement of the internal standard is not affected by method or matrix interferences. Some rec- ommended internal standards are listed in Table 3.

    - Prepare calibration standards at a minimum of three concentration levels for each parameter by carefully adding 20.0 L of one or more secondary dilution standards to 50, 250, or 500 mL of reagent water. A 25-L syringe with a 0.006 in. ID needle should be used for this operation. One of the calibra- tion standards should be at a concentration near, but above, the  MDL (Table 1) and  the other concentrations should correspond to the expected range of  concentrations  found in real samples or should define the working range of the GC/MS system. These aqueous standards can be stored up to 24 h, if held in sealed vials with zero headspace as described in Section 9.2. If not so stored, they must be discarded after 1 h.

    - Prepare a spiking solution con- taining each of the internal standards  using the procedures described in Sections 6.5 and

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 624

6.6. It is recommended that the secondary di- lution standard be prepared at a concentra- tion of 15 g/mL of each internal standard compound. The addition of 10 L of this standard to 5.0 mL of sample or calibration standard would be equivalent to 30 g/L.

    - Analyze each calibration standard according to Section 11, adding 10 L of in- ternal standard spiking solution directly to the syringe (Section 11.4). Tabulate the area response of the characteristic m/z against concentration for each compound and inter- nal standard, and calculate response factors (RF) for each compound using Equation 1.

As Cis 

## RF 

Ais Cs 

Equation   1

where:

As  = Area of the characteristic m/z for the parameter to be measured.

Ais  = Area of the characteristic m/z for the inernal standard.

Cis = Concentration of the internal standard.

Cs  = Concentration of the parameter to be measured.

If the RF value over the working range is a constant (<35% RSD), the RF can be assumed to be invariant and the average RF can be used for calculations. Alternatively, the re- sults can be used to plot a calibration curve of response ratios, As/Ais, vs. RF.

  - The working calibration curve or RF must be verified on each working day by the measurement of a QC check sample.

    - Prepare the QC check sample as de- scribed in Section 8.2.2.

    - Analyze the QC check sample accord- ing to the method beginning in Section 10.

    - For each parameter, compare the re- sponse (Q) with the corresponding calibra- tion acceptance criteria found in Table 5. If the responses for all parameters of interest fall within the designated ranges, analysis of actual samples can begin. If any individual Q falls outside the range, proceed according to Section 7.4.4.

NOTE: The large number of parameters in Table 5 present  a  substantial  probability that one or more will not meet the  calibra- tion acceptance criteria when all parameters are analyzed.

    - Repeat the test only for those pa- rameters that failed to meet the calibration acceptance criteria. If the response for a pa- rameter does not fall within the range  in this second test, a new calibration curve or RF must be prepared for that parameter ac- cording to Section 7.3.

  - Quality Control

8.1  Each laboratory that uses this method is required to operate a formal quality  con- trol program. The minimum requirements of

this program consist of an initial demonstra- tion of laboratory capability and an ongoing analysis of spiked samples to evaluate and document data quality. The laboratory must maintain records to document the quality of data that is generated. Ongoing data quality checks are compared with established per- formance criteria to determine if the results of analyses meet the performance character- istics of the method. When results of sample spikes indicate atypical method perform- ance, a quality control check  standard  must be analyzed to confirm that the measure- ments were performed in an in-control mode of operation.

    - The analyst must make an initial, one-time, demonstration of the ability to generate acceptable accuracy and precision with this method. This  ability  is  established as described in Section 8.2.

    - In recognition of advances that are occurring in chromatography, the analyst is permitted certain  options  (detailed  in  Sec- tion 11.1) to improve the separations or lower the cost of measurements. Each time such a modification is made to the method, the ana- lyst is required to repeat the procedure in Section 8.2.

    - Each day, the analyst must analyze a reagent water blank to demonstrate that interferences from the analytical system are under control.

    - The laboratory must, on an ongoing basis, spike and analyze a minimum of 5% of all samples to monitor and evaluate labora- tory data quality. This procedure is de- scribed in Section 8.3.

    - The laboratory must, on an ongoing basis, demonstrate through the analyses of quality control  check standards  that  the op- eration of the measurement system is in con- trol.  This  procedure  is  described  in  Section

8.4. The frequency of the check standard analyses is equivalent to 5% of all samples analyzed but may be reduced if spike recov- eries from samples (Section 8.3) meet all specified quality control criteria.

    - The laboratory must spike all sam- ples with surrogate standards to monitor continuing laboratory performance. This procedure is described in Section 8.5.

    - The laboratory must maintain per- formance records to document the quality of data that is generated. This procedure is de- scribed in Section 8.6.

  - To establish the ability to generate acceptable accuracy and precision, the ana- lyst must perform the following operations.

    - A quality control (QC) check sample concentrate is required containing each pa- rameter of  interest  at a  concentration  of  10

g/mL in methanol. The QC check sample concentrate must be obtained from the U.S. Environmental Protection Agency, Environ- mental Monitoring and Support Laboratory in Cincinnati, Ohio, if available. If not avail- able from that source, the QC check sample

#### Pt. 136, App. A, Meth. 624

concentrate must be obtained from another external source. If not available from either source above, the QC check sample con- centrate must be prepared by the laboratory using stock standards prepared independ- ently from those used for calibration.

    - Prepare a QC check sample to con- tain 20 g/L of each parameter by adding 200

L of QC check sample concentrate to 100 mL of reagent water.

    - Analyze four 5-mL aliquots of the well-mixed  QC  check  sample  according  to the method beginning in Section 10.

    - Calculate the average recovery (X¯ ) in

g/L, and the standard deviation of the re- covery (s) in g/L, for each parameter of in- terest using the four results.

    - For each parameter compare s and X¯

with the corresponding acceptance criteria for   precision   and   accuracy,   respectively,

found in Table 5. If s and X¯  for all param-

eters of interest meet the acceptance cri- teria, the system performance is acceptable and analysis of actual samples can begin. If any individual s exceeds the precision limit

or any individual X¯  falls outside the range

for accuracy, the system performance is un- acceptable for that parameter.

NOTE: The large number of parameters in Table 5 present  a  substantial  probability that one or more will fail at least one of the acceptance criteria when all parameters are analyzed.

    - When one or more of the parameters tested fail at least one of the acceptance cri- teria, the analyst must proceed according to Section 8.2.6.1 or 8.2.6.2.

      - Locate and correct the source of the problem and repeat the test for all pa- rameters of interest beginning with Section 8.2.3.

      - Beginning with Section 8.2.3, repeat the test only for those  parameters  that failed to meet criteria. Repeated failure, however, will confirm a  general  problem with the measurement system. If this occurs, locate and correct the source of the problem and repeat the test for all compounds of in- terest beginning with Section 8.2.3.

  - The laboratory must, on an ongoing basis, spike at least 5% of the samples from each sample site being monitored to assess accuracy. For laboratories analyzing 1 to 20 samples per month, at least one  spiked  sam- ple per month is required.

    - The concentration of the spike in the sample should be determined as follows:

      - If, as in compliance monitoring, the concentration of a specific parameter in the sample is being checked against a regu- latory concentration limit, the spike should be at that limit or 1 to 5 times higher than the background concentration determined in Section 8.3.2, whichever concentration would be larger.

      - If the concentration of a specific parameter   in   the   sample   is   not   being

#### 40 CFR Ch. I (7–1–17 Edition)

checked against a limit specific to that pa- rameter, the spike should be at 20 g/L or 1 to 5  times  higher than  the  background  con- centration determined in Section 8.3.2, whichever concentration would be larger.

    - Analyze one 5-mL sample aliquot to determine the background concentration (B) of each parameter. If necessary, prepare a new QC check sample concentrate (Section 8.2.1) appropriate for the background con- centrations in the sample. Spike a second 5- mL sample aliquot with 10 L of the QC check sample concentrate and analyze it to determine   the   concentration   after   spiking

(A) of each parameter. Calculate each per- cent recovery (P) as 100(A¥B)%/T, where T is the known true value of the spike.

    - Compare the percent recovery (P) for each parameter with the corresponding QC acceptance criteria found in Table 5. These acceptance criteria wer calculated to include an allowance for error in measurement of both the background and spike concentra- tions, assuming a spike  to  background  ratio of 5:1. This error will be accounted for to the extent that the analyst’s spike to back- ground ratio approaches 5:1. 7 If spiking was performed at a concentration lower than 20

g/L, the analyst must use either the QC ac- ceptance criteria in Table 5, or optional QC acceptance criteria calculated  for the  spe- cific spike concentration. To calculate op- tional acceptance  criteria  for  the  recoveryof a parameter: (1) Calculate accuracy (X) using the equation in Table 6,  substituting the spike concentration (T) for C; (2) cal- culate  overall  precision  (S)  using  the  equa-

tion in Table 6, substituting Xfor X¯ ; (3) cal-

culate the range for recovery at the spike concentration as (100 X/T) (2.44(100 S/T)%. 7

    - If any individual P falls outside the designated range for recovery, that param- eter has failed the acceptance criteria. A check standard containing each parameter that failed the criteria must be analyzed as described in Section 8.4.

  - If any parameter fails the acceptance criteria for recovery in Section 8.3, a QC check standard containing each parameter that failed must be prepared and analyzed.

NOTE: The frequency for the required anlaysis of a QC check standard will depend upon the number of parameters being simul- taneously tested, the complexity of the sam- ple matrix, and the performance of the lab- oratory. If the entire list of parameters in Table 5 must be measured in the sample in Section 8.3, the probability that the analysis of a QC check standard will be required is high. In this case the QC  check  standard should be routinely analyzed with the spiked sample.

    - Prepare the QC check standard by adding 10 L of QC check sample concentrate (Section 8.2.1 or 8.3.2) to 5 mL of reagent water.  The  QC  check  standard  needs  only  to

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 624

contain the parameters that  failed  criteria in the test in Section 8.3.

    - Analyze the QC check standard to determine the concentration measured (A) of each parameter. Calculate each percent re- covery (PS) as 100 (A/T)%, where T is the true value of the standard concentration.

    - Compare the percent recovery (PS) for each parameter with the corresponding QC acceptance criteria found in Table 5. Only parameters that failed the test in Section 8.3 need to be compared with these  criteria.  If the recovery of any such parameter falls out- side the designated range, the laboratory performance for that parameter is judged to be out of control, and the problem must be immediately identified and corrected. The analytical result for that parameter in the unspiked sample is suspect  and may not  be reported for regulatory compliance purposes.

  - As a quality control check, the labora- tory must spike all samples with the surro- gate standard spiking solutions as described in Section 11.4, and calculate the percent re- covery of each surrogate compound.

  - As part of the QC program for the lab- oratory, method accuracy for wastewater samples must be assessed and records must be maintained. After the analysis of five spiked wastewater samples as in Section 8.3,

calculate  the  average  percent  recovery  (P¯ )

and the standard deviation of the percent re- covery (sp). Express the accuracy assessment

as a percent recovery interval from P¯ —2sp  to P¯ + 2sp. If P¯ = 90% and sp = 10%, for example,

the accuracy interval is expressed as 70– 110%. Update the accuracy  assessment  for each parameter a  regular  basis  (e.g.  after each five to  ten  new  accuracy  measure- ments).

  - It is recommended that the laboratory adopt additional quality assurance practices for use  with  this method.  The  specific  prac- tices that  are  most  productive  depend  upon the needs of the laboratory and the nature of the samples. Field duplicates may be ana- lyzed to assess the precision of the environ- mental measurements. Whenever  possible, the laboratory should analyze standard ref- erence materials and participate in relevant performance evaluation studies.

  - Sample Collection, Preservation, and Handling

  - All samples must be iced or refrig- erated from the time of collection until anal- ysis. If the  sample  contains  residual  chlo- rine, add sodium thiosulfate preservative (10 mg/40 mL is sufficient for up to 5 ppm Cl2) to the empty sample bottle just prior to ship- ping to  the sampling  site. EPA Methods  330.4 and 330.5 may be used for measurement of re- sidual chlorine. 8 Field test kits  are  available for  this  purpose.

  - Grab samples must be collected in glass containers having a total volume of at least  25  mL.  Fill  the  sample  bottle  just  to

overflowing in such a manner that no air bubbles pass through the sample as the bot- tle is being filled. Seal  the bottle so that no air bubbles are entrapped in it. If  preserva- tive has been added, shake vigorously for 1 min. Maintain the hermetic seal on the sam- ple bottle until time of analysis.

  - Experimental evidence indicates that some aromatic compounds, notably benzene, toluene, and ethyl benzene are susceptible to rapid biological degradation under certain environmental conditions. 3 Refrigeration alone may not be adequate to preserve these compounds in wastewaters for more than seven days. For this reason, a separate sam- ple should be collected, acidified, and ana- lyzed when these aromatics are to be deter- mined. Collect about 500 mL of sample in a clean container. Adjust the pH of the sample to about 2 by adding 1 + 1 HCl while stirring vigorously, Check pH with narrow range (1.4 to 2.8) pH paper. Fill a sample container as described in Section 9.2.

  - All samples must be analyzed  within 14 days of collection. 3

  - Daily GC/MS Performance Tests

  - At the beginning of each day that analyses are to be performed, the GC/MS sys- tem must be checked to see if acceptable performance criteria are achieved for BFB. 9 The performance test must be passed before any samples, blanks, or standards are ana- lyzed, unless the instrument has met the DFTPP test described  in Method 625  earlier in the day. 10

  - These performance tests require the following instrumental parameters:

Electron  Energy:  70  V  (nominal) Mass Range: 20 to 260 amu

Scan  Time:  To  give  at  least  5  scans  per peak but not to exceed 7 s per scan.

  - At the beginning of each day, inject 2

L of BFB solution directly on the column. Alternatively,  add  2  L  of  BFB  solution  to

5.0 mL of reagent water or standard solution and analyze the solution according to sec- tion 11. Obtain a background-corrected mass spectrum of BFB and confirm that all  the key m/z criteria in Table  2  are  achieved.  If all the criteria are  not achieved, the analyst must retune the mass spectrometer and re- peat  the  test  until  all  criteria  are  achieved.

  - Sample Purging and Gas Chromatography

    - Table 1 summarizes the recommended operating conditions for the gas chro- matograph. Included in this table are reten- tion times and MDL that can be achieved under these conditions. An example of the separations achieved by  this  column  is shown in Figure 5. Other packed columns or chromatographic conditions may be used if the requirements of Section 8.2 are met.

#### Pt. 136, App. A, Meth. 624

    - After achieving the key m/z abun- dance criteria in Section 10, calibrate the system daiy as described in Section 7.

    - Adjust the purge gas (helium) flow rate to 40 mL/min. Attach the  trap  inlet  to the purging device, and set the purge and trap system to purge (Figure 3). Open the sy- ringe valve located on the purging device sample introduction needle.

    - Allow the sample to come to ambient temperature prior to introducing it into the syringe. Remove the plunger from a 5-mL sy- ringe and attach a closed syringe valve. Open the sample bottle (or standard) and carefully pour the sample into the syringe barrel  to just short of overflowing. Replace the sy- ringe plunger and compress the sample. Open the syringe valve and vent any residual air while adjusting the sample volume to 5.0 mL. Since this process of taking an aliquot de- stroys the validity of the sample for future analysis, the analyst should fill a second sy- ringe at this time to protect against possible loss of data. Add 10.0 L of the surrogate spiking solution (Section 6.7) and 10.0 L of the internal standard spiking solution (Sec- tion 7.3.2) through the valve bore, then close the valve. The surrogate and internal stand- ards may be mixed and added as a single spiking  solution.

    - Attach the syringe-syringe valve as- sembly to the syringe valve on the purging device. Open the syringe valves and  inject the sample into the purging chamber.

    - Close both valves and purge the sam- ple for 11.0 0.1 min at ambient temperature.

    - After the 11-min purge time, attach the trap to the chromatograph, adjust the purge and trap system to the desorb mode (Figure 4), and begin to temperature pro- gram the gas chromatograph. Introduce the trapped materials to the GC column by rap- idly heating the trap to 180 C while backflushing the trap with an inert gas be- tween 20 and 60 mL/min for 4 min. If rapid heating of the trap cannot  be  achieved,  the GC cloumn must be used as a secondary trap by cooling it to 30 C (subambient tempera- ture, if problems persist) instead of  the  ini- tial program temperature of 45 C.

    - While the trap is being desorbed into the gas chromatograph, empty the purging chamber using the sample introduction sy- ringe. Wash the chamber with two 5-mL flushes of reagent water.

    - After desorbing the sample for 4 min, recondition the trap by returning the purge and trap system to the purge mode. Wait 15 s then close the syringe valve on the purging device to begin gas flow through the trap. The trap temperature should  be  maintained at 180 C. After approximately 7 min, turn off the trap heater and open the syringe valve to stop the gas flow through the trap. When the trap is cool, the next sample can be ana- lyzed.

#### 40 CFR Ch. I (7–1–17 Edition)

    - If the response for any m/z exceeds the working range of the system, prepare a dilution of the sample with reagent water from the aliquot in the second syringe and reanalyze.

  - Qualitative Identification

  - Obtain EICPs for the primary m/z (Table 4) and at least two secondary masses for each parameter of interest. The following criteria must be met to make a qualitative identification:

    - The characteristic masses of each parameter of interest must maximize in the same or within one scan of each other.

    - The retention time must fall within

30 s of the retention time of the authentic compound.

    - The relative peak heights of the three characteristic masses in the EICPs must fall within 20% of the relative inten- sities of these masses in a reference mass spectrum. The reference mass spectrum can be obtained from a standard analyzed in the GC/MS system or from a reference library.

12.2 Structural isomers that have very similar mass spectra and less than 30 s dif- ference in retention time, can be explicitly identified only if the resolution between au- thentic isomers in a standard mix is accept- able. Acceptable resolution is achieved if the baseline to valley height between the iso- mers is less than 25% of the sum of the two peak heights. Otherwise, structural isomers are identified as isomeric pairs.

  - Calculations

  - When a parameter has been identi- fied, the quantitation of that parameter should be based on the integrated abundance from the EICP of the primary characteristic m/z given in Table 4. If the sample produces an interference for the primary m/z, use a secondary characteristic m/z to quantitate.

Calculate the concentration in the sample using the response factor (RF) determined in Section 7.3.3 and Equation 2.

As Cis 

## Concentration (g/L) 

Ais RF

Equation   2

where:

AS = Area of the characteristic m/z for the parameter or surrogate standard to be measured.

Ais = Area of the characteristic m/z for the internal standard.

Cis = Concentration of the internal standard.

  - Report results in g/L without correc- tion for recovery data. All QC data obtained should be reported with the sample results.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 624

  - Method Performance

  - The method detection limit (MDL) is defined as the minimum concentration of a substance that can be measured and reported with 99% confidence that the value is above zero. 1 The MDL concentrations listed  in Table 1 were obtained using reagent water. 11 Similar results were achieved using rep- resentative wastewaters. The MDL actually achieved in a given analysis will vary de- pending on instrument sensitivity and ma- trix  effects.

  - This method was tested by 15 labora- tories using reagent water, drinking water, surface water, and industrial wastewaters spiked at six concentrations over the range 5–600 g/L. 12 Single operator precision, over- all precision, and method accuracy were found to be directly related to the concentra- tion of the parameter and essentially inde- pendent of the sample matrix. Linear equa- tions to describe these relationships are pre- sented in Table 5.

REFERENCES

- 40 CFR part 136, appendix B.

- Bellar,  T.A.,  and  Lichtenberg,  J.J. ‘‘De- termining   Volatile   Organics   at   Microgram- per-Litre   Levels   by   Gas   Chromatography,’’ Journal American Water Works Association, 66, 739 (1974).

- Bellar, T.A., and Lichtenberg, J.J. ‘‘Semi-Automated Headspace Analysis of Drinking Waters and Industrial Waters for Purgeable Volatile  Organic Compounds,  ’’ Measurement of Organic Pollutants in Water and Wastewater, C.E. Van Hall, editor, American Society for Testing and Materials, Philadelphia, PA. Special Technical Publica- tion 686, 1978.

- ‘‘Carcinogens—Working With Carcino- gens,’’ Department of Health, Education, and Welfare, Public Health Service, Center for Disease Control, National Institute for Occu- pational Safety and Health, Publication No. 77–206, August 1977.

- ‘‘OSHA Safety and Health Standards, General Industry,’’ (29 CFR part 1910), Occu- pational Safety and Health Administration, OSHA 2206 (Revised, January 1976).

- ‘‘Safety in Academic Chemistry Labora- tories,’’ American Chemical Society Publica- tion, Committee on Chemical Safety, 3rd Edition, 1979.

- Provost,  L.P.,  and  Elder,  R.S.  ‘‘Interpre- tation   of   Percent   Recovery   Data,’’   American Laboratory, 15, 58–63  (1983).  (The  value  2.44 used  in  the  equation  in  Section  8.2.3  is  two times the value 1.22 derived in this report.)

- ‘‘Methods 330.4 (Titrimetric, DPD-FAS) and 330.5 (Spectrophotometric, DPD) for Chlorine, Total Residual,’’ Methods for Chemical Analysis of Water and Wastes, EPA–600/4–79–020, U.S. Environmental Pro- tection   Agency,   Environmental   Monitoring

and   Support   Laboratory,   Cincinnati,   Ohio 45268, March 1979.

- Budde, W.L., and Eichelberger, J.W. ‘‘Performance Tests for the Evaluation of Computerized Eas Chromatography/Mass Spectrometry Equipment and Laboratories,’’ EPA–600/4–80–025, U.S. Environmental Pro- tection Agency, Environmental Monitoring and Support Laboratory, Cincinnati, Ohio 45268, April 1980.

- Eichelberger, J.W., Harris, L.E., and Budde, W.L. ‘‘Reference Compound to  Cali- brate Ion Abundance Measurement in Gas Chromatography—Mass Spectrometry Sys- tems,’’ Analytical Chemistry, 47, 995–1000 (1975).

- ‘‘Method Detection Limit for Methods 624 and 625,’’ Olynyk, P., Budde, W.L., and Eichelberger, J.W. Unpublished report, May 14, 1980.

- ‘‘EPA Method Study 29 EPA Method 624—Purgeables,’’ EPA 600/4–84–054, National Technical Information Service, PB84–209915, Springfield, Virginia 22161, June 1984.

13.‘‘Method Performance Data for Method 624,’’ Memorandum from R. Slater and T. Pressley, U.S. Environmental Protection Agency, Environmental Monitoring and Sup- port Laboratory, Cincinnati, Ohio 45268, Jan- uary 17, 1984.

TABLE 1—CHROMATOGRAPHIC CONDITIONS AND

| Parameter | Retention time (min) | Method detection limit (g/L) |
| --- | --- | --- |
| Chloromethane .............................. | 2.3 | nd |
| Bromomethane .............................. | 3.1 | nd |
| Vinyl chloride ................................. | 3.8 | nd |
| Chloroethane ................................. | 4.6 | nd |
| Methylene chloride ........................ | 6.4 | 2.8 |
| Trichlorofluoromethane .................. | 8.3 | nd |
| 1,1-Dichloroethene ........................ | 9.0 | 2.8 |
| 1,1-Dichloroethane ........................ | 10.1 | 4.7 |
| trans-1,2-Dichloroethene ............... | 10.8 | 1.6 |
| Chloroform ..................................... | 11.4 | 1.6 |
| 1,2-Dichloroethane ........................ | 12.1 | 2.8 |
| 1,1,1-Trichloroethane .................... | 13.4 | 3.8 |
| Carbon tetrachloride ...................... | 13.7 | 2.8 |
| Bromodichloromethane ................. | 14.3 | 2.2 |
| 1,2-Dichloroproane ........................ | 15.7 | 6.0 |
| cis-1,3-Dichloropropene ................ | 15.9 | 5.0 |
| Trichloroethene .............................. | 16.5 | 1.9 |
| Benzene ........................................ | 17.0 | 4.4 |
| Dibromochloromethane ................. | 17.1 | 3.1 |
| 1,1,2-Trichloroethane .................... | 17.2 | 5.0 |
| trans-1,3-Dichloropropene ............. | 17.2 | nd |
| 2-Chloroethylvinlyl ether ................ | 18.6 | nd |
| Bromoform ..................................... | 19.8 | 4.7 |
| 1,1,2,2-Tetrachloroethane ............. | 22.1 | 6.9 |
| Tetrachloroethene ......................... | 22.2 | 4.1 |
| Toluene .......................................... | 23.5 | 6.0 |
| Chlorobenzene .............................. | 24.6 | 6.0 |
| Ethyl benzene ................................ | 26.4 | 7.2 |
| 1,3-Dichlorobenzene ..................... | 33.9 | nd |
| 1,2-Dichlorobenzene ..................... | 35.0 | nd |

METHOD DETECTION LIMITS

#### Pt. 136, App. A, Meth. 624

TABLE 1—CHROMATOGRAPHIC CONDITIONS AND

METHOD DETECTION LIMITS—Continued

#### 40 CFR Ch. I (7–1–17 Edition)

TABLE 4—CHARACTERISTIC MASSES FOR

PURGEABLE ORGANICS

| Parameter | Retention time (min) | Method detection limit (g/L) |
| --- | --- | --- |
| 1,4-Dichlorobenzene ..................... | 35.4 | nd |
| Parameter | Pri- mary | Secondary |
| Chloromethane ............................. | 50 | 52. |
| Bromomethane ............................. | 94 | 96. |
| Vinyl chloride ................................ | 62 | 64. |
| Chloroethane ................................ | 64 | 66. |
| Methylene chloride ........................ | 84 | 49, 51, and 86. |
| Trichlorofluoromethane ................. | 101 | 103. |
| 1,1-Dichloroethene ........................ | 96 | 61 and 98. |
| 1,1-Dichloroethane ........................ | 63 | 65, 83, 85, 98, |
|  |  | and 100. |
| trans-1,2-Dichloroethene .............. | 96 | 61 and 98. |
| Chloroform .................................... | 83 | 85. |
| 1,2-Dichloroethane ........................ | 98 | 62, 64, and 100. |
| 1,1,1-Trichloroethane .................... | 97 | 99, 117, and 119. |
| Carbon tetrachloride ..................... | 117 | 119 and 121. |
| Bromodichloromethane ................. | 127 | 83, 85, and 129. |
| 1,2-Dichloropropane ..................... | 112 | 63, 65, and 114. |
| trans-1,3-Dichloropropene ............ | 75 | 77. |
| Trichloroethene ............................. | 130 | 95, 97, and 132. |
| Benzene ........................................ | 78 |  |
| Dibromochloromethane ................. | 127 | 129, 208, and |
|  |  | 206. |
| 1,1,2-Trichloroethane .................... | 97 | 83, 85, 99, 132, |
|  |  | and 134. |
| cis-1,3-Dichloropropene ................ | 75 | 77. |
| 2-Chloroethylvinyl ether ................ | 106 | 63 and 65. |
| Bromoform .................................... | 173 | 171, 175, 250, |
|  |  | 252, 254, and |
|  |  | 256. |
| 1,1,2,2-Tetrachloroethane ............. | 168 | 83, 85, 131, 133, |
|  |  | and 166. |
| Tetrachloroethene ......................... | 164 | 129, 131, and |
|  |  | 166. |
| Toluene ......................................... | 92 | 91. |
| Chlorobenzene .............................. | 112 | 114. |
| Ethyl benzene ............................... | 106 | 91. |
| 1,3-Dichlorobenzene ..................... | 146 | 148 and 113. |
| 1,2-Dichlorobenzene ..................... | 146 | 148 and 113. |
| 1,4-Dichlorobenzene ..................... | 146 | 148 and 113. |

Column conditions: Carbopak B (60/80 mesh) coated with 1% SP–1000 packed in a 6 ft by 0.1 in. ID glass column with helium carrier gas at 30 mL/min. flow rate. Column tempera- ture held at 45 C for 3 min., then programmed at 8 C/min. to 220 C and held for 15 min.

nd = not determined.

TABLE 2—BFB KEY M/Z ABUNDANCE CRITERIA

| Mass | m/z Abundance criteria |
| --- | --- |
| 50 ........................................... 75 ........................................... 95 ........................................... 96 ........................................... 173 ......................................... 174 ......................................... 175 ......................................... 176 ......................................... 177 ......................................... | 15 to 40% of mass 95. 30 to 60% of mass 95. Base Peak, 100% Relative Abundance. 5 to 9% of mass 95. <2% of mass 174. >50% of mass 95. 5 to 9% of mass 174. >95% but <101% of mass 174. 5 to 9% of mass 176. |

TABLE 3—SUGGESTED SURROGATE AND

INTERNAL STANDARDS

| Compound | Reten- tion time (min) a | Pri- mary m/z | Secondary masses |
| --- | --- | --- | --- |
| Benzene d-6 .......................... | 17.0 | 84 | 174, 176 |
| 4-Bromofluorobenzene .......... | 28.3 | 95 |  |
| 1,2-Dichloroethane d-4 .......... | 12.1 | 102 |  |
| 1,4-Difluorobenzene .............. | 19.6 | 114 | 63, 88 |
| Ethylbenzene d-5 .................. | 26.4 | 111 |  |
| Ethylbenzene d-10 ................ | 26.4 | 98 |  |
| Fluorobenzene ....................... | 18.4 | 96 | 70 |
| Pentafluorobenzene .............. | 23.5 | 168 |  |
| Bromochloromethane ............ | 9.3 | 128 | 49, 130, 51 |
| 2-Bromo-1-chloropropane ..... | 19.2 | 77 | 79, 156 |
| 1, 4-Dichlorobutane ............... | 25.8 | 55 | 90, 92 |

a For chromatographic conditions, see Table 1.

TABLE 5—CALIBRATION AND QC ACCEPTANCE CRITERIA—METHOD 624 A

| Parameter | Range for Q (/g/L) | Limit for s (/g/L) | Range for X¯ (/g/L) | Range for P, Ps (%) |
| --- | --- | --- | --- | --- |
| Benzene .......................................................................................... | 12.8¥27.2 | 6.9 | 15.2¥26.0 | 37¥151 |
| Bromodichloromethane ................................................................... | 13.1¥26.9 | 6.4 | 10.1¥28.0 | 35¥155 |
| Bromoform ....................................................................................... | 14.2¥25.8 | 5.4 | 11.4¥31.1 | 45¥169 |
| Bromomethane ................................................................................ | 2.8¥37.2 | 17.9 | D¥41.2 | D¥242 |
| Carbon tetrachloride ........................................................................ | 14.6¥25.4 | 5.2 | 17.2¥23.5 | 70¥140 |
| Chlorobenzene ................................................................................ | 13.2¥26.8 | 6.3 | 16.4¥27.4 | 37¥160 |
| Chloroethane ................................................................................... | 7.6¥32.4 | 11.4 | 8.4¥40.4 | 14¥230 |
| 2-Chloroethylvinyl ether .................................................................. | D¥44.8 | 25.9 | D¥50.4 | D¥305 |
| Chloroform ....................................................................................... | 13.5¥26.5 | 6.1 | 13.7¥24.2 | 51¥138 |
| Chloromethane ................................................................................ | D¥40.8 | 19.8 | D¥45.9 | D¥273 |
| Dibromochloromethane ................................................................... | 13.5¥26.5 | 6.1 | 13.8¥26.6 | 53¥149 |
| 1,2-Dichlorobenzene ....................................................................... | 12.6¥27.4 | 7.1 | 11.8¥34.7 | 18¥190 |
| 1,3-Dichlorobenzene ....................................................................... | 14.6¥25.4 | 5.5 | 17.0¥28.8 | 59¥156 |
| 1,4-Dichlorobenzene ....................................................................... | 12.6¥27.4 | 7.1 | 11.8¥34.7 | 18¥190 |
| 1,1-Dichloroethane .......................................................................... | 14.5¥25.5 | 5.1 | 14.2¥28.5 | 59¥155 |
| 1,2-Dichloroethane .......................................................................... | 13.6¥26.4 | 6.0 | 14.3¥27.4 | 49¥155 |
| 1,1-Dichlorothene ............................................................................ | 10.1¥29.9 | 9.1 | 3.7¥42.3 | D¥234 |
| trans-1,2-Dichloroethene ................................................................. | 13.9¥26.1 | 5.7 | 13.6¥28.5 | 54¥156 |

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 624

TABLE 5—CALIBRATION AND QC ACCEPTANCE CRITERIA—METHOD 624 A—Continued

| Parameter | Range for Q (/g/L) | Limit for s (/g/L) | Range for X¯ (/g/L) | Range for P, Ps (%) |
| --- | --- | --- | --- | --- |
| 1,2-Dichloropropane ........................................................................ | 6.8¥33.2 | 13.8 | 3.8¥36.2 | D¥210 |
| cis-1,3-Dichloropropene .................................................................. | 4.8¥35.2 | 15.8 | 1.0¥39.0 | D¥227 |
| trans-1,3-Dichloropropene ............................................................... | 10.0¥30.0 | 10.4 | 7.6¥32.4 | 17¥183 |
| Ethyl benzene ................................................................................. | 11.8¥28.2 | 7.5 | 17.4¥26.7 | 37¥162 |
| Methylene chloride .......................................................................... | 12.1¥27.9 | 7.4 | D¥41.0 | D¥221 |
| 1,1,2,2-Tetrachloroethane ............................................................... | 12.1¥27.9 | 7.4 | 13.5¥27.2 | 46¥157 |
| Tetrachloroethene ........................................................................... | 14.7¥25.3 | 5.0 | 17.0¥26.6 | 64¥148 |
| Toluene ........................................................................................... | 14.9¥25.1 | 4.8 | 16.6¥26.7 | 47¥150 |
| 1,1,1-Trichloroethane ...................................................................... | 15.0¥25.0 | 4.6 | 13.7¥30.1 | 52¥162 |
| 1,1,2-Trichloroethane ...................................................................... | 14.2¥25.8 | 5.5 | 14.3¥27.1 | 52¥150 |
| Trichloroethene ............................................................................... | 13.3¥26.7 | 6.6 | 18.6¥27.6 | 71¥157 |
| Trichlorofluoromethane ................................................................... | 9.6¥30.4 | 10.0 | 8.9¥31.5 | 17¥181 |
| Vinyl chloride ................................................................................... | 0.8¥39.2 | 20.0 | D¥43.5 | D¥251 |

Q= Concentration measured in QC check sample, in g/L (Section 7.5.3).

s= Standard deviation of four recovery measurements, in g/L (Section 8.2.4). X¯ = Average recovery of four recovery measurements, in g/L (Section 8.2.4).

P, Ps= Percent recovery measured, (Section 8.3.2, Section 8.4.2). D= Detected; result must be greater than zero.

a Criteria were calculated assuming a QC check sample concentration of 20 g/L.

NOTE: These criteria are based directly upon the method performance data in Table 6. Where necessary, the limits for recov- ery have been broadened to assure applicability of the limits to concentrations below those used to develop Table 6.

TABLE 6—METHOD ACCURACY AND PRECISION AS FUNCTIONS OF CONCENTRATION—METHOD 624

| Parameter | Accuracy, as recovery, X (g/L) | Single analyst precision, sr (g/L) | Overall preci- sion, S(g/L) |
| --- | --- | --- | --- |
| Benzene ............................................................................................................ | 0.93C + 2.00 | 0.26X¯ ¥1.74 | 0.25X¯ ¥1.33 |
| Bromodichloromethane ..................................................................................... | 1.03C¥1.58 | 0.15X¯ + 0.59 | 0.20X¯ + 1.13 |
| Bromoform ......................................................................................................... | 1.18C¥2.35 | 0.12X¯ + 0.36 | 0.17X¯ + 1.38 |
| Bromomethane a ................................................................................................ | 1.00C | 0.43X¯ | 0.58X¯ |
| Carbon tetrachloride .......................................................................................... | 1.10C¥1.68 | 0.12X¯ + 0.25 | 0.11X¯ + 0.37 |
| Chlorobenzene .................................................................................................. | 0.98C + 2.28 | 0.16X¯ ¥0.09 | 0.26X¯ ¥1.92 |
| Chloroethane ..................................................................................................... | 1.18C + 0.81 | 0.14X¯ + 2.78 | 0.29X¯ + 1.75 |
| 2–Chloroethylvinyl ether a .................................................................................. | 1.00C | 0.62X¯ | 0.84X¯ |
| Chloroform ......................................................................................................... | 0.93C + 0.33 | 0.16X¯ + 0.22 | 0.18X¯ + 0.16 |
| Chloromethane .................................................................................................. | 1.03C + 0.81 | 0.37X¯ + 2.14 | 0.58X¯ + 0.43 |
| Dibromochloromethane ..................................................................................... | 1.01C¥0.03 | 0.17X¯ ¥0.18 | 0.17X¯ + 0.49 |
| 1,2–Dichlorobenzene b ...................................................................................... | 0.94C + 4.47 | 0.22X¯ ¥1.45 | 0.30X¯ ¥1.20 |
| 1,3–Dichlorobenzene ......................................................................................... | 1.06C + 1.68 | 0.14X¯ ¥0.48 | 0.18X¯ ¥0.82 |
| 1,4–Dichlorobenzene b ...................................................................................... | 0.94C + 4.47 | 0.22X¯ ¥1.45 | 0.30X¯ ¥1.20 |
| 1,1–Dichloroethane ........................................................................................... | 1.05C + 0.36 | 0.13X¯ ¥0.05 | 0.16X¯ + 0.47 |
| 1,2–Dichloroethane ........................................................................................... | 1.02C + 0.45 | 0.17X¯ ¥0.32 | 0.21X¯ ¥0.38 |
| 1,1–Dichloroethene ........................................................................................... | 1.12C + 0.61 | 0.17X¯ + 1.06 | 0.43X¯ ¥0.22 |
| trans–1,2,–Dichloroethene ................................................................................ | 1.05C + 0.03 | 0.14X¯ + 0.09 | 0.19X¯ + 0.17 |
| 1,2–Dichloropropane a ....................................................................................... | 1.00C | 0.33X¯ | 0.45X¯ |
| cis–1,3–Dichloropropene a ................................................................................. | 1.00C | 0.38X¯ | 0.52X¯ |
| trans–1,3–Dichloropropene a ............................................................................. | 1.00C | 0.25X¯ | 0.34X¯ |
| Ethyl benzene .................................................................................................... | 0.98C + 2.48 | 0.14X¯ + 1.00 | 0.26X¯ ¥1.72 |
| Methylene chloride ............................................................................................ | 0.87C + 1.88 | 0.15X¯ + 1.07 | 0.32X¯ + 4.00 |
| 1,1,2,2–Tetrachloroethane ................................................................................ | 0.93C + 1.76 | 0.16X¯ + 0.69 | 0.20X¯ + 0.41 |
| Tetrachloroethene ............................................................................................. | 1.06C + 0.60 | 0.13X¯ ¥0.18 | 0.16X¯ ¥0.45 |
| Toluene .............................................................................................................. | 0.98C + 2.03 | 0.15X¯ ¥0.71 | 0.22X¯ ¥1.71 |
| 1,1,1–Trichloroethane ........................................................................................ | 1.06C + 0.73 | 0.12X¯ ¥0.15 | 0.21X¯ ¥0.39 |
| 1,1,2–Trichloroethane ........................................................................................ | 0.95C + 1.71 | 0.14X¯ + 0.02 | 0.18X¯ + 0.00 |
| Trichloroethene .................................................................................................. | 1.04C + 2.27 | 0.13X¯ + 0.36 | 0.12X¯ + 0.59 |
| Trichloroflouromethane ...................................................................................... | 0.99C + 0.39 | 0.33X¯ ¥1.48 | 0.34X¯ ¥0.39 |
| Vinyl chloride ..................................................................................................... | 1.00C | 0.48X¯ | 0.65X¯ |

X¯ = Expected recovery for one or more measurements of a sample containing a concentration of C, in g/L.

Sr = Expected single analyst standard deviation of measurements at an average concentration found ofX¯ , in g/L. S= Expected interlaboratory standard deviation of measurements at an average concentration found ofX¯ , in g/L. C = True value for the concentration, in g/L.

X¯ = Average recovery found for measurements of samples containing a concentration of C, in g/L.

a Estimates based upon the performance in a single laboratory. 13

b Due to chromatographic resolution problems, performance statements for these isomers are based upon the sums of their concentrations.

#### Pt. 136, App. A, Meth. 624

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 624

Pt. 136, App. A, Meth. 624

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 625

METHOD 625—BASE/NEUTRALS AND ACIDS

- Scope and Application

  - This method covers the determination of a number of organic compounds that  are partitioned into an organic solvent and are amenable to gas chromatography. The pa- rameters listed in Tables 1 and 2 may be qualitatively and quantitatively determined using this method.

  - The method may be extended to in- clude the parameters listed in Table 3. Benzi- dine can be subject to oxidative losses during solvent concentration. Under the alkaline conditions of the extraction step, a–BHC, g– BHC, endosulfan I and II, and endrin are sub- ject	to	decomposition.

Hexachlorocyclopentadiene is subject to thermal decomposition in the inlet of the gas chromatograph, chemical reaction in ace- tone solution, and photochemical decomposi- tion. N-nitrosodimethylamine is difficult to separate from the solvent under the chromatographic conditions described. N- nitrosodiphenylamine decomposes in the gas chromatographic inlet and cannot be sepa- rated from diphenylamine. The preferred method for each of these parameters is listed in Table 3.

  - This is a gas chromatographic/mass spectrometry (GC/MS) method 2 14  applicable to the determination of the compounds listed in Tables 1, 2, and 3 in municipal and indus- trial discharges as provided under 40 CFR 136.1.

#### Pt. 136, App. A, Meth. 625

  - The method detection limit (MDL, de- fined in Section 16.1) 1 for each parameter is listed in Tables 4 and 5. The MDL for a spe- cific wastewater may differ from those  list- ed, depending upon the nature of inter- ferences in the sample matrix.

  - Any modification to this method, be- yond those expressly permitted, shall be con- sidered as a major modification subject to application and approval of alternate test procedures under 40 CFR 136.4 and 136.5. De- pending upon the nature of the modification and the extent of intended use, the applicant may be required to demonstrate that the modifications will produce equivalent results when applied to relevant wastewaters.

  - This method is restricted to use by or under the supervision of analysts experi- enced in  the  use  of  a  gas  chromatograph/ mass spectrometer and in the interpretation of mass spectra. Each analyst must dem- onstrate the ability to generate acceptable results with this method using the procedure described in Section 8.2.

- Summary of Method

2.1 A measured volume of sample, approxi- mately 1–L, is serially extracted with meth- ylene chloride at a pH greater than 11 and again at a pH less than 2 using a separatory funnel or a continuous extractor. 2 The meth- ylene chloride extract is  dried,  concentrated to a volume of 1 mL, and analyzed by GC/MS. Qualitative identification of the  parameters in the extract is performed using the reten- tion time and the  relative  abundance  of three characteristic masses (m/z). Quan- titative analysis is performed using internal standard techniques with a single char- acteristic m/z.

- Interferences

  - Method interferences may be caused by contaminants in solvents, reagents, glass- ware, and other sample processing hardware that lead to discrete artifacts  and/or  ele- vated baselines in the total ion current pro- files. All of these  materials  must  be  rou- tinely demonstrated to be free from inter- ferences under the conditions of the analysis by running laboratory reagent blanks as de- scribed in Section 8.1.3.

    - Glassware must be scrupulously cleaned. 3 Clean all glassware as soon as pos- sible after use by rinsing with the last sol- vent used in it. Solvent rinsing should be fol- lowed by detergent washing with hot water, and rinses with tap water and distilled water. The glassware should then be drained dry, and heated in a muffle furnace at 400 C for 15 to 30 min. Some thermally stable ma- terials, such as PCBs, may not be eliminated by this treatment. Solvent rinses with ace- tone and pesticide quality hexane may be substituted for the muffle furnace heating. Thmrough rinsing with such solvents usually

#### 40 CFR Ch. I (7–1–17 Edition)

eliminates PCB interference. Volumetric ware should not be heated in a muffle fur- nace. After drying and cooling, glassware should be sealed and stored in a clean envi- ronment to prevent any accumulation of dust or other contaminants. Store inverted or capped with aluminum foil.

    - The use of high purity reagents and solvents helps to minimize interference prob- lems. Purification of solvents  by  distillation in all-glass systems may be required.

  - Matrix interferences may be caused by contaminants that are co-extracted from the sample. The extent of matrix interferences will vary considerably from source to source, depending upon the nature and diversity  of the industrial complex or municipality being sampled.

  - The base-neutral extraction may cause significantly reduced recovery of phenol, 2- methylphenol, and 2,4-dimethylphenol. The analyst must recognize that results obtained under these conditions are minimum con- centrations.

  - The packed gas chromatographic col- umns recommended for the basic fraction may not exhibit sufficient resolution for cer- tain isomeric pairs including the following: anthracene and phenanthrene; chrysene and benzo(a)anthracene;	and

benzo(b)fluoranthene		and benzo(k)fluoranthene.	The	gas chromatographic retention time and mass spectra for these pairs of compounds are not sufficiently different to make an unambig- uous identification. Alternative techniques should be used to identify and quantify these specific compounds, such as Method 610.

  - In samples that contain an inordinate number of interferences, the use of chemical ionization (CI) mass spectrometry may make identification easier. Tables 6 and 7 give characteristic CI ions for most of the com- pounds covered by this method. The use of CI mass spectrometry to support electron ion- ization (EI) mass spectrometry is encouraged but not required.

- Safety

  - The   toxicity   or   carcinogenicity   of each reagent used in this method have not been precisely defined; however, each chem- ical compound should be treated as a poten- tial health hazard. From this viewpoint, ex- posure to these chemicals must be reduced to the lowest possible level by whatever means available. The laboratory is responsible for maintaining   a   current   awareness   file   of OSHA  regulations  regarding  the  safe  han- dling of the chemicals specified in this meth- od. A reference file of material data handling sheets should also be made available to all personnel involved in the chemical analysis. Additional  references  to  laboratory  safety are available and have been identified 4M6 for the information of the analyst.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 625

  - The following parameters covered by this method have been  tentatively  classified as known or suspected, human or mamma- lian carcinogens: benzo(a)anthracene, benzi- dine, 3,3-dichlorobenzidine, benzo(a)pyrene, a-BHC,	b-BHC,	d-BHC,	g-BHC, dibenzo(a,h)anthracene,			N- nitrosodimethylamine, 4,4-DDT, and poly- chlorinated biphenyls (PCBs). Primary standards of these toxic compounds  should be prepared in a hood. A NIOSH/MESA ap- proved toxic gas respirator should be worn when the analyst handles high  concentra- tions of these toxic compounds.

- Apparatus and Materials

  - Sampling equipment, for discrete or composit  sampling.

    - Grab sample bottle—1-L or 1-gt, amber glass, fitted with a screw cap lined with Teflon. Foil may be substituted for Tef- lon if the sample is not corrosive. If amber bottles are not available, protect samples from light. The bottle and cap liner must be washed, rinsed with acetone or methylene chloride, and dried before use to minimize contamination.

    - Automatic sampler (optional)—The sampler must incorporate glass sample con- tainers for the collection of a minimum of 250 mL of sample. Sample containers must be kept refrigerated at 4 C and protected from light during compositing. If the sampler uses a peristaltic pump, a minimum length of compressible silicone rubber tubing may be used. before use, however, the compressible tubing should be throughly rinsed with methanol, followed by repeated rinsings with distilled water to minimize the potential for contamination of the sample. An integrating flow meter is required to collect flow propor- tional  composites.

  - Glassware (All specifications are sug- gested. Catalog numbers are included for il- lustration only.):

    - Separatory funnel—2–L, with Teflon stopcock.

    - Drying column—Chromatographic column, 19 mm ID, with coarse frit

    - Concentrator tube, Kuderna-Dan- ish—10-mL, graduated (Kontes K–570050–1025 or equivalent). Calibration must  be  checked at the volumes employed in the test. Ground glass stopper is used to prevent evaporation of  extracts.

    - Evaporative flask, Kuderna-Danish— 500-mL (Kontes K–57001–0500 or equivalent). Attach  to  concentrator  tube  with  springs.

    - Snyder column, Kuderna-Danish— Three all macro (Kontes K–503000–0121 or equivalent).

    - Snyder column, Kuderna-Danish— Two-ball macro (Kontes K–569001–0219 or equivalent).

    - Vials—10 to 15-mL, amber glass, with Teflon-lined screw cap.

    - Continuous liquid—liquid extractor— Equipped with Teflon or glass connecting joints and stopcocks requiring  no  lubrica- tion. (Hershberg-Wolf Extractor, Ace Glass Company, Vineland, N.J., P/N 6841–10 or equivalent.)

  - Boiling chips—Approximately 10/40 mesh. Heat to 400 C for 30 min of Soxhlet ex- tract  with  methylene  chloride.

  - Water bath—Heated, with concentric ring cover, capable of temperature control (2 C). The bath should be used in a hood.

  - Balance—Analytical, capable of accu- rately weighing 0.0001 g.

  - GC/MS system:

    - Gas Chromatograph—An analytical system complete  with  a  temperature  pro- grammable gas chromatograph and all re- quired accessores including syringes, analyt- ical columns, and gases. The injection port must be designed  for on-column  injection when using packed columns and for splitless injection when using capillary columns.

    - Column for base/neutrals—1.8 m long

    - 2 mm ID glass, packed with 3% SP–2250 on Supelcoport (100/120 mesh) or equivalent. This column was used to develop the method performance statements in Section 16. Guidelines for the use of alternate column packings are provided in Section 13.1.

    - Column for acids—1.8 m long 2 mm

ID glass, packed with 1% SP–1240DA on Supelcoport (100/120 mesh) or equivalent. This column was used to develop the method performance statements in Section 16. Guidelines for the use of alternate column packings are given in Section 13.1.

    - Mass spectrometer—Capable of scan- ning from 35 to 450 amu every 7 s or less, uti- lizing a 70 V (nominal) electron energy in the electron impact ionization mode, and pro- ducing a mass spectrum which meets all the criteria in Table 9 when 50 ng of decafluorotriphenyl phosphine (DFTPP; bis(perfluorophenyl) phenyl phosphine) is in- jected through the GC inlet.

    - GC/MS interface—Any GC to MS interface that gives acceptable calibration points at 50 ng per injection for each of the parameters of interest and achieves all ac- ceptable performance  criteria  (Section  12) may be used. GC to MS interfaces con- structed of all glass or glass-lined  materials are recommended. Glass can be  deactivated by  silanizing  with  dichlorodimethylsilane.

    - Data system—A computer system must be interfaced to the mass spectrometer that allows the contiluous acquisition and storage on machine-readable media of  all mass spectra obtained throughout the dura- tion of the chromatographic program. The computer must have software that allows searching any GC/MS data file for specific m/ z and plotting such m/z abundances versus time or scan number. This type of plot is de- fined as an Extracted Ion Current Profile (EICP). Software  must also  be  available that

#### Pt. 136, App. A, Meth. 625

allows integrating the abundance in any EICP between specified time or scan number limits.

- Reagents

  - Reagent water—Reagent water is de- fined as a water in which an  interferent  is not observed at the  MDL  of  the  parameters of  interest.

  - Sodium hydroxide solution (10 N)— Dissolve 40 g of NaOH (ACS) in reagent water and dilute to 100 mL.

  - Sodium thiosulfate—(ACS) Granular.

  - Sulfuric acid (1 + 1)—Slowly, add  50 mL of  H2SO4 (ACS, sp.  gr.  1.84) to  50  mL of reagent water.

  - Acetone, methanol, methlylene chlo- ride—Pesticide quality or equivalent.

  - Sodium sulfate—(ACS) Granular, an- hydrous. Purify by heating at 400 C for 4 h in a shallow tray.

  - Stock standard solutions (1.00 g/L)— standard solutions can be prepared from pure standard materials or purchased as certified solutions.

    - Prepare stock  standard solutions by accurately weighing about 0.0100 g of pure material. Dissolve the material in pesticide quality acetone or other suitable solvent and dilute  to  volume  in   a   10-mL   volumetric flask. Larger volumes can be used at the con- venience of the analyst. When compound pu- rity is assayed to be  96%  or  greater,  the weight may be used without correction to calculate the concentration of the stock standard. Commercially prepared stock standards may  be  used  at  any  concentration if they are certified  by  the  manufacturer  or by an independent source.

    - Transfer the stock standard solu- tions into Teflon-sealed screw-cap bottles. Store at 4 C and protect from light. Stock standard solutions should be checked fre- quently for signs of degradation or evapo- ration, especially just prior to preparing calibration standards from them.

    - Stock standard solutions must be re- placed after six months, or sooner if com- parison with quality control check samples indicate a problem.

  - Surrogate standard spiking solution— Select a minimum of three surrogate com- pounds from Table 8. Prepare a surrogate standard spiking solution containing each selected surrogate compound at a concentra- tion of 100 g/mL in acetone. Addition of 1.00 mL of this solution to 1000 mL of sample is equivalent to a concentration of 100 g/L of each surrogate standard. Store the spiking solution at 4 C in Teflon-sealed glass con- tainer. The solution should be checked fre- quently for stability. The solution must be replaced after six months, or sooner if com- parison with quality control check standards indicates a problem.

  - DFTPP standard—Prepare a 25 g/mL

solution of DFTPP in acetone.

#### 40 CFR Ch. I (7–1–17 Edition)

  - Quality control check sample con- centrate—See Section 8.2.1.

- Calibration

  - Establish gas chromatographic oper- ating parameters equivalent to those indi- cated in Table 4 or 5.

  - Internal standard calibration proce- dure—To use this approach, the analyst must select three or more internal standards that are similar in analytical behavior to the compounds of interest. The analyst must fur- ther demonstrate that the measurement of the internal standards is not affected by method or matrix interferences. Some rec- ommended internal standards are listed in Table 8. Use the base peak m/z as the pri- mary m/z for quantification of the standards. If interferences are noted, use one of the next two most intense m/z quantities for quantification.

    - Prepare calibration standards at a minimum of three concentration levels  for each parameter of interest by adding appro- priate volumes of one or more stock stand- ards to a volumetric flask. To each calibra- tion standard or standard mixture, add a known constant amount of one or more in- ternal standards, and dilute to volume with acetone. One of the calibration standards should be at a concentration near, but above, the MDL and the other concentrations should correspond to the expected range of concentrations found in real samples or should define the working range of the GC/ MS system.

    - Using injections of 2 to 5 L, analyze

each calibration standard according to Sec- tion 13 and tabulate the area of the primary characteristic m/z (Tables 4 and 5) against concentration for each compound and inter- nal standard. Calculate response factors (RF) for each compound using Equation 1.

As Cis 

## RF 

Ais Cs 

Equation   1

where:

As  = Area of the characteristic m/z for the parameter to be measured.

Ais  = Area of the characteristic m/z for the internal standard.

Cis  = Concentration of the internal standard (g/L).

Cs   =  Concentration  of  the  parameter  to  be measured (g/L).

If the RF value over the working range is a constant (<35% RSD), the RF can be assumed to be invariant and the average RF can be used for calculations. Alternatively, the re- sults can be used to plot a calibration curve of response ratios, As/Ais, vs. RF.

  - The working calibration curve or RF

must be verified on each working day by the

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 625

measurement of one or more calibration standards. If the response for any parameter varies from the predicted response by more than 20%, the test must be repeated uning a fresh calibration standard. Alternatively,  a new calibration curve must be prepared for that compound.

- Quality Control

  - Each laboratory that uses this method is required to operate a formal quality  con- trol program. The minimum requirements of this program consist of an initial demonstra- tion of laboratory capability and an ongoing analysis of spiked samples to evaluate and document data quality. The laboratory must maintain records to document the quality of data that is generated. Ongoing data quality checks are compared with established per- formance criteria to determine if the results of analyses meet the performance character- istics of the method. When results of sample spikes indicate atypical method perform- ance, a quality control check  standard  must be analyzed to confirm that the measure- ments were performed in an in-control mode of operation.

    - The analyst must make an initial, one-time, demonstration of the ability to generate acceptable accuracy and precision with this method. This  ability  is  established as described in Section 8.2.

    - In recognition of advances that are occuring in chromatography, the analyst is permitted certain  options  (detailed  in  Sec- tions 10.6 and 13.1) to improve the separa- tions or lower the cost of measurements. Each time such a modification is  made  to the method, the analyst is required to repeat the procedure in Section 8.2.

    - Before processing any samples, the analyst must analyze a  reagent  water  blank to demonstrate that interferences from the analytical system and glassware are under control. Each time a set of samples is ex- tracted or reagents are changed, a reagent water blank must be processed as a safe- guard  against  laboratory  contamination.

    - The laboratory must, on an ongoing basis, spike and analyze a minimum of 5% of all samples to monitor and evaluate labora- tory data quality. This procedure is de- scribed in Section 8.3.

    - The laboratory must, on an ongoing basis, demonstrate through the analyses of quality control  check standards  that  the op- eration of the measurement system is in con- trol.  This  procedure  is  described  in  Section

8.4. The frequency of the check standard analyses is equivalent to 5% of all samples analyzed but may be reduced if spike recov- eries from samples (Section 8.3) meet all specified quality control criteria.

    - The laboratory must maintain per- formance records to document the quality of data that is generated. This procedure is de- scribed in Section 8.5.

  - To establish the ability to generate acceptable accuracy and precision, the ana- lyst must perform the following operations.

    - A quality control (QC) check sample concentrate is required containing each pa- rameter of interest at a concentration of 100

g/mL in acetone. Multiple solutions may be required. PCBs and multicomponent pes- ticides may be omitted from this test. The QC check sample concentrate must be ob- tained from the U.S. Environmental Protec- tion Agency, Environmental Monitoring and Support Laboratory in Cincinnati, Ohio, if available. If not available from that source, the QC check sample concentrate must be obtained from another external source. If not available from either source above, the QC check sample concentrate must be prepared by the laboratory using stock standards pre- pared independently from those used for cali- bration.

    - Using a pipet, prepare QC check sam- ples at a concentration of 100 g/L by adding

1.00 mL of QC check sample concentrate to each of four 1–L aliquots of reagent water.

    - Analyze the well-mixed QC check samples according to the  method   beginning in Section 10 or 11.

    - Calculate the average recovery (X) in

g/L, and the standard deviation of the re- covery (s) in g/L, for each parameter using the four results.

    - For each parameter compare s and X with the corresponding acceptance criteria for precision and accuracy, respectively, found in Table 6. If s and X for all param- eters of interest meet the acceptance cri- teria, the system performance is acceptable and analysis of actual samples can begin. If any individual s exceeds the precision limit or any individual X falls outside the range for accuracy, the system performance is un- acceptable for that parameter.

NOTE: The large number of parameters in Table 6 present  a  substantial  probability that one or more will fail at least one of the acceptance criteria when all parameters are analyzed.

    - When one or more of the parameters tested fail at least one of the acceptance cri- teria, the analyst must proceed according to Section 8.2.6.1 or 8.2.6.2.

      - Locate and correct the source of the problem and repeat the test for all pa- rameters of interest beginning with Section 8.2.2.

      - Beginning with Section 8.2.2, repeat the test only for those  parameters  that failed to meet criteria. Repeated failure, however, will confirm a  general  problem with the measurement system. If this occurs, locate and correct the source of the problem and repeat the test for all compounds of in- terest beginning with Section 8.2.2.

  - The laboratory must, on an ongoing basis, spike at least 5% of the samples from each sample site being monitored to assess

#### Pt. 136, App. A, Meth. 625

accuracy. For laboratories analyzing 1 to 20 samples per month, at least one spiked sam- ple per month is required.

    - The concentration of the spike in the sample should be determined as follows:

    - If, as in compliance monitoring, the concentration of a specific parameter in the sample is being checked against a regulatory concentration limit, the spike should be at that limit or 1 to 5 times higher than the background concentration determined in Section 8.3.2, whichever concentration would be larger.

      - If the concentration of a specific parameter in the sample  is  not  being checked against a limit specific to that pa- rameter, the spike should be at 100 g/L or 1 to 5  times  higher than  the  background  con- centration determined in Section 8.3.2, whichever concentration would be larger.

      - If it is impractical to determine background levels before spiking (e.g., max- imum holding times will be exceeded), the spike concentration should be (1) the regu- latory concentration limit, if any; or, if none

(2) the larger of either 5  times  higher  than the expected background  concentration  or 100 g/L.

    - Analyze one sample aliquot to deter- mine the background concentration (B) of each parameter. If necessary, prepare a new QC check sample concentrate (Section 8.2.1) appropriate for the background concentra- tions in the sample. Spike a second sample aliquot with 1.0 mL of the QC check sample concentrate and analyze it to determine the concentration after spiking (A) of each pa- rameter. Calculate each percent recovery (P) as 100(A¥B)%/T, where T is the known true value of the spike.

    - Compare the percent recovery (P) for each parameter with the corresponding QC acceptance criteria found in Table 6. These acceptance criteria were calculated to in- clude an allowance for error in measurement of both the background and spike concentra- tions, assuming a spike  to  background  ratio of 5:1. This error will be accounted for to the extent that the analyst’s spike to back- ground ratio approaches 5:1. 7 If spiking was performed at a concentration lower than 100

g/L, the analyst must use either the QC ac- ceptance criteria in Table 6, or optional QC acceptance criteria calculated  for the  spe- cific spike concentration. To calculate op- tional acceptance criteria for the recovery of a parameter: (1) Calculate accuracy (X) using the equation in Table 7,  substituting the spike concentration (T) for C; (2) cal- culate  overall  precision  (S)  using  the  equa-

tion in Table 7, substituting Xfor X¯ ; (3) cal-

culate the range for recovery at the spike concentration as (100 X/T)2.44(100 S/T)% 7

    - If any individual P falls outside the designated range for recovery, that param- eter has failed the acceptance criteria. A check  standard  containing  each  parameter

#### 40 CFR Ch. I (7–1–17 Edition)

that failed the criteria must be analyzed as described in Section 8.4.

  - If any parameter fails the acceptance criteria for recovery in Section 8.3, a QC check standard containing each parameter that failed must be prepared and analyzed.

NOTE: The frequency for the required anal- ysis of a QC check standard will depend upon the number of parameters being simulta- neously tested, the complexity of the sample matrix, and the performance of the labora- tory. If the entire list of single-component parameters in Table 6 must be measured in the sample in Section 8.3, the probability that the analysis of a QC check standard will be required is high. In this case the QC check standard should be routinely analyzed with the spike sample.

    - Prepare the QC check standard by adding 1.0 mL of QC check sample con- centrate (Section 8.2.1 or 8.3.2) to 1 L of rea- gent water. The QC check standard needs only to contain the parameters that failed criteria in the test in Section 8.3.

    - Analyze the QC check standard to determine the concentration measured (A) of each parameter. Calculate each percent re- covery (PS) as 100 (A/T)%, where T is the true value of the standard concentration.

    - Compare the percent recovery (Ps) for each parameter with the corresponding QC acceptance criteria found in Table 6. Only parameters that failed the test in Section 8.3 need to be compared with these  criteria.  If the recovery of any such parameter falls out- side the designated range, the laboratory performance for that parameter is judged to be out of control, and the problem must be immediately identified and corrected. The analytical result for that parameter in the unspiked sample is suspect  and may not  be reported for regulatory compliance purposes.

  - As part of the QC program for the lab- oratory, method accuracy for wastewater samples must be assessed and records must be maintained. After the analysis of five spiked wastewater samples as in Section 8.3,

calculate  the  average  percent  recovery  (P¯ )

and the standard deviation of the percent re- covery (sp). Express the accuracy assessment

as a percent interval from P¯ ¥2sp to P¯ + 2sp. If P¯  = 90% and sp = 10%, for example, the ac-

curacy interval is expressed as 70¥110%. Up- date the accuracy assessment for each pa- rameter on a regular basis (e.g. after  each five to ten new accuracy measurements).

  - As a quality control check, the labora- tory must spike all samples with the surro- gate standard spiking solution  as  described in Section 10.2, and calculate the percent re- covery of each surrogate compound.

  - It is recommended that the laboratory adopt additional quality assurance practices for use with this method. The specific prac- tices that are most productive depend upon the needs of the laboratory and the nature of

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 625

the samples. Field duplicates may be ana- lyzed to assess the precision of the environ- mental measurements. Whenever  possible, the laboratory should analyze standard ref- erence materials and participate in relevant performance evaluation studies.

- Sample Collection, Preservation, and Handling

  - Grab samples must be collected  in glass containers. Conventional sampling practices 8 should be followed, except  that the bottle must not be prerinsed with sample before collection. Composite samples should be collected in refrigerated  glass  containers in accordance with the requirements of the program. Automatic sampling equipment must be as free as possible of Tygon tubing and other potential sources of contamina- tion.

  - All sampling must be iced or refrig- erated at 4 C from the time of collection until extraction. Fill the sample bottles and, if residual chlorine is present, add 80 mg of sodium thiosulfate per liter of sample and mix well. EPA Methods 330.4 and 330.5 may be used for measurement of residual chlo- rine. 9 Field test kits are available for this purpose.

  - All samples must be extracted within 7 days of collection and completely analyzed within 40 days of extraction.

- Separatory Funnel Extraction

  - Samples are usually extracted using separatory funnel  techniques.  If emulsions will prevent achieving acceptable solvent re- covery with separatory funnel extractions, continuous extraction (Section 11) may be used. The separatory funnel extraction scheme described below assumes a sample volume of 1 L. When sample volumes of 2 L are to be extracted, use 250, 100, and 100-mL volumes of methylene chloride for the serial extraction of the base/neutrals and 200, 100, and 100-mL volumes of methylene chloride for the acids.

  - Mark the water meniscus on the side of the sample bottle  for  later  determination of sample volume. Pour the entire sample into a  2–L separatory  funnel. Pipet  1.00 mL of the surrogate standard spiking solution into the separatory funnel and mix  well. Check the pH of the sample with wide-range pH paper  and  adjust  to  pH>11  with  sodium hydroxide  solution.

  - Add 60 mL of methylene chloride  to the sample bottle, seal, and shake for 30 s to rinse the inner surface. Transfer the solvent to the separatory funnel and extract the sample by shaking the funnel for 2 min. with periodic venting to release excess pressure. Allow the organic layer to separate from the water phase for a minimum of 10 min. If the emulsion interface between layers is more than   one-third   the   volume   of   the   solvent

layer, the analyst must employ mechanical techniques to complete the phase separation. The optimum technique depends upon the sample, but may include  stirring,  filtration of the emulsion through glass wool, cen- trifugation, or other physical methods. Col- lect the methylene chloride extract in a 250- mL Erlenmeyer flask. If the emulsion cannot be broken (recovery of less than 80% of the methylene chloride, corrected for the water solubility of  methylene  chloride),  transfer the sample, solvent, and emulsion into the extraction chamber of a continuous extrac- tor and proceed as described in Section 11.3.

  - Add a second 60-mL volume of meth- ylene chloride to the sample bottle and re- peat the extraction procedure a second time, combining the extracts in the  Erlenmeyer flask. Perform a third extraction in the same manner. Label the combined extract as the base/neutral fraction.

  - Adjust the pH of the aqueous phase to less than 2 using sulfuric acid. Serially ex- tract the acidified aqueous phase three times with 60-mL aliquots of methylene chloride. Collect and combine the extracts in a 250-mL Erlenmeyer flask and label the combined ex- tracts as the acid fraction.

  - For each fraction, assemble a Kuderna-Danish (K-D) concentrator by at- taching a 10-mL concentrator tube to a 500- mL evaporative flask. Other concentration devices or techniques may be used in place of the K-D concentrator if the requirements of Section 8.2 are met.

  - For each fraction, pour the combined extract through a solvent-rinsed drying col- umn containing about 10 cm of anhydrous so- dium sulfate, and collect the extract in  the K-D  concentrator.  Rinse  the  Erlenmeyer flask and column with 20 to 30 mL of meth- ylene chloride to complete the quantitative transfer.

  - Add one or two clean boiling chips and attach a three-ball Snyder column to the evaporative flask for each fraction. Prewet each Snyder column by adding about 1 mL of methylene chloride to  the  top.  Place  the  K- D apparatus on a hot water bath (60 to 65 C) so that the concentrator tube is partially immersed in the hot water, and the entire lower rounded surface of the flask is bathed with hot vapor. Adjust  the  vertical  position of the apparatus and the water temperature as required to complete the concentration in

15 to 20 min. At the proper rate of distilla- tion the balls of the column will actively chatter but the chambers will not flood with condensed solvent. When the apparent vol- ume of liquid reaches 1 mL, remove the K-D apparatus from the water  bath  and  allow  it to drain and cool for at least 10 min. Remove the Snyder column and rinse  the  flask  and its lower joint into the concentrator tube with 1 to 2 mL of  methylene  chloride.  A  5- mL syringe is recommended for this oper- ation.

#### Pt. 136, App. A, Meth. 625

  - Add another one or two clean boiling chips to the concentrator tube for each frac- tion and attach a two-ball micro-Snyder col- umn. Prewet the Snyder column by adding about 0.5 mL of methylene chloride to  the top. Place the K-D apparatus on a hot water bath (60 to 65 C) so that the concentrator tube is partially immersed in hot water. Ad- just the vertical position of the apparatus and the water temperature as required to complete the concentration in  5  to  10  min. At the proper rate of distillation the balls of the column will actively chatter but the chambers will not flood with condensed sol- vent. When the apparent volume of liquid reaches about 0.5 mL, remove the K-D appa- ratus from the water bath and allow it to drain and cool for at least  10  min.  Remove the Snyder column and rinse  the  flask  and its lower joint into the concentrator tube with approximately 0.2 mL of acetone or methylene chloride. Adjust the  final  volume to 1.0 mL with the solvent. Stopper the con- centrator tube and store refrigerated if fur- ther processing will not be performed imme- diately. If the extracts will be stored longer than two days, they should be transferred to Teflon-sealed screw-cap vials and labeled base/neutral or acid fraction as appropriate.

  - Determine the original sample vol- ume by refilling the sample bottle to the mark and transferring the liquid to  a  1000- mL graduated cylinder. Record the sample volume to the nearest 5 mL.

- Continuous Extraction

  - When experience with a sample from a given source indicates that a serious emul- sion problem will result or an emulsion is en- countered using a separatory funnel in Sec- tion 10.3, a continuous extractor should be used.

  - Mark the water meniscus  on  the  side of the sample  bottle  for  later  determination of sample volume. Check the pH  of  the  sam- ple with wide-range pH paper and  adjust  to pH >11 with sodium hydroxide solution. Transfer the sample to the continuous ex- tractor and using a pipet, add 1.00 mL of sur- rogate standard spiking solution  and  mix well. Add 60 mL of methylene chloride to the sample bottle,  seal,  and  shake  for  30  s  to rinse the inner surface.  Transfer  the  solvent to  the  extractor.

  - Repeat the sample bottle rinse  with an additional 50 to 100-mL portion of meth- ylene chloride and add the rinse to the ex- tractor.

  - Add 200 to 500 mL of methylene chlo- ride to the distilling flask, add sufficient re- agent water to ensure proper operation, and extract for 24 h. Allow to  cool,  then  detach the distilling flask.  Dry,  concentrate,  and seal the extract as in Sections 10.6 through 10.9.

  - Charge  a  clean  distilling  flask  with

500  mL  of  methylene  chloride  and  attach  it

#### 40 CFR Ch. I (7–1–17 Edition)

to the continuous extractor. Carefully, while stirring, adjust the pH of the aqueous phase to less than 2 using sulfuric acid. Extract for 24 h. Dry, concentrate,  and  seal  the  extract as in Sections 10.6 through 10.9.

- Daily GC/MS Performance Tests

12.1 At the beginning of each day that analyses are to be performed, the GC/MS sys- tem must be checked to see if acceptable performance criteria  are  achieved  for DFTPP. 10 Each day that benzidine is to be determined, the tailing factor criterion de- scribed in Section 12.4 must be achieved. Each day that the acids are to be deter- mined,  the  tailing  factor  criterion  in  Section

12.5 must be achieved.

  - These performance tests require the following instrumental parameters:

Electron  Energy:  70  V  (nominal) Mass Range: 35 to 450 amu

Scan Time: To give at least 5 scans per peak but not to exceed 7 s per scan.

  - DFTPP performance test—At the be- ginning of each day, inject 2 L (50 ng) of DFTPP standard solution. Obtain a back- ground-corrected mass spectra of  DFTPP and confirm that all the key m/z criteria in Table 9 are achieved. If all  the  criteria  are not achieved, the analyst must retune the mass spectrometer  and repeat  the test  until all criteria are achieved. The performance criteria must be achieved before any sam- ples, blanks, or standards are analyzed. The taililg factor tests in Sections 12.4 and 12.5 may be performed simultaneously with the DFTPP   test.

  - Column performance  test  for base/ neutrals—At the beginning of each day  that the base/neutral fraction is to be  analyzed for benzidine, the benzidine tailing  factor must be calculated. Inject 100 ng of benzidine either separately or as a part of a standard mixture that may contain DFTPP and cal- culate the tailing factor. The benzidine  tail- ing factor must be less than 3.0. Calculation of  the  tailing  factor  is  illustrated  in  Figure

- 11 Replace the column packing if the tail- ing factor criterion cannot be achieved.

  - Column performance test for  acids— At the beginning of each day  that  the  acids are to be determined, inject 50 ng of pentachlorophenol either separately or as a part of a standard mix that may  contain DFTPP.	The	tailing	factor	for pentachlorophenol must be less than 5. Cal- culation of the tailing factor is illustrated in Figure 13. 11 Replace the column packing  if the tailing factor  criterion  cannot  be achieved.

  - Gas Chromatography/Mass Spectrometry

    - Table 4 summarizes the recommended gas chromatographic operating  conditions for the base/neutral fraction. Table 5 summa- rizes the recommended gas chromatographic

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 625

operating conditions for the acid fraction. Included in these tables are retention times and MDL that can be achieved under these conditions. Examples of the separations achieved by these columns are shown in Fig- ures 1 through 12. Other packed or capillary (open-tubular) columns or chromatographic conditions may be used  if  the  requirements of Section 8.2 are met.

    - After conducting the GC/MS perform- ance tests in Section 12, calibrate the system daily as described in Section 7.

    - The internal standard must be added to sample extract and mixed thoroughly im- mediately before it is injected into the in- strument. This procedure minimizes losses due to adsorption, chemical reaction or evaporation.

    - Inject 2 to 5 L of the sample extract or standard into the GC/MS system using the solvent-flush technique. 12 Smaller (1.0  L) volumes may be injected if automatic de- vices are employed. Record the volume in- jected to the nearest 0.05 L.

    - If the response for any m/z exceeds the working range of the GC/MS system, di- lute the extract and reanalyze.

    - Perform all qualitative and quan- titative measurements as described  in  Sec- tions 14 and 15. When the extracts are not being used for analyses, store them  refrig- erated at 4 C, protected from light  in  screw- cap vials equipped with unpierced  Teflon- lined  septa.

  - Qualitative Identification

14.1 Obtain EICPs for the primary m/z and the two other masses listed in Tables 4 and

- See Section 7.3 for masses to be used with internal and surrogate standards. The fol- lowing criteria must be met to make a quali- tative  identification:

    - The characteristic masses of each parameter of interest must maximize in the same or within one scan of each other.

    - The retention time must fall within

30 s of the retention time of the authentic compound.

    - The relative peak heights of the three characteristic masses in the EICPs must fall within 20% of the relative inten- sities of these masses in a reference mass spectrum. The reference mass spectrum can be obtained from a standard analyzed in the GC/MS system or from a reference library.

14.2 Structural isomers that have very similar mass spectra and less than 30 s dif- ference in retention time, can be explicitly identified only if the resolution between au- thentic isomers in a standard mix is accept- able. Acceptable resolution is achieved if the baseline to valley height between the iso- mers is less than 25% of the sum of the two peak heights. Otherwise, structural isomers are identified as isomeric pairs.

  - Calculations

  - When a parameter  has  been  identi- fied, the quantitation of  that  parameter  will be based on the integrated abundance  from the  EICP  of   the   primary   characteristic   m/z in Tables 4 and 5. Use the base peak m/z for internal and surrogate standards. If the  sam- ple produces an interference for the primary m/z, use a  secondary characteristic m/z  to quantitate.

Calculate the concentration in the sample using the response factor (RF) determined in Section 7.2.2 and Equation 3.

As Is 

Concentration (g/L) 

Ais RFVo 

Equation   3

where:

As = Area of the characteristic m/z for the parameter or surrogate standard to be measured.

Ais = Area of the characteristic m/z for the internal standard.

Is = Amount of internal standard added to each extract (g).

Vo = Volume of water extracted (L).

  - Report results in g/L without correc- tion for recovery data. All QC data obtained should be reported with the sample results.

  - Method Performance

  - The method detection limit (MDL) is defined as the minimum concentration of a substance that can be measured and reported with 99% confidence that the value is above zero. 1 The MDL  concentrations listed  in Ta- bles 4 and 5 were obtained using reagent water. 13  The MDL actually achieved  in  a given analysis will vary depending on instru- ment  sensitivity  and  matrix  effects.

  - This method was tested by 15 labora- tories using reagent water, drinking water, surface water, and industrial wastewaters spiked at six concentrations over the range 5 to 1300 g/L. 14 Single operator precision, overall precision, and method accuracy were found to be directly related to the concentra- tion of the parameter and essentially inde- pendent of the sample matrix. Linear equa- tions to describe these relationships are pre- sented in Table 7.

  - Screening Procedure for 2,3,7,8- Tetrachlorodibenzo-p-dioxin  (2,3,7,8–TCDD)

  - If the sample must be screened for the presence of 2,3,7,8–TCDD, it is rec- ommended that the reference material not be handled in the laboratory unless extensive safety precautions are employed. It is suffi- cient to analyze the base/neutral extract by selected ion monitoring (SIM) GC/MS tech- niques, as follows:

    - Concentrate the base/neutral ex- tract to a final volume of 0.2 ml.

#### Pt. 136, App. A, Meth. 625

    - Adjust the temperature of the base/ neutral column (Section 5.6.2) to 220 C.

    - Operate the mass spectrometer to acquire data in the  SIM  mode  using  the  ions at m/z 257, 320 and 322 and a dwell time no greater than 333 milliseconds per mass.

    - Inject 5 to 7 L of the base/neutral extract. Collect SIM data for a total of 10 min.

    - The possible presence of 2,3,7,8– TCDD is indicated if all three masses exhibit simultaneous peaks at any point in the se- lected ion current profiles.

    - For each occurrence where the pos- sible presence of 2,3,7,8–TCDD is indicated, calculate and retain the  relative  abundances of each of the three masses.

  - False positives to this test may be caused by the presence of single or coeluting combinations of compounds whose mass spectra contain all of these masses.

  - Conclusive results of the presence and concentration level of 2,3,7,8–TCDD can be obtained only from a properly equipped lab- oratory through the use of EPA Method 613 or other approved alternate test procedures.

REFERENCES

- 40 CFR part 136, appendix B.

- ‘‘Sampling and Analysis Procedures for Screening of Industrial Effluents for Priority Pollutants,’’ U.S. Environmental Protection Agency, Environmental Monitoring and Sup- port Laboratory, Cincinnati, Ohio 45268, March 1977, Revised April 1977. Available from Effluent Guidelines Division, Wash- ington, DC 20460.

- ASTM Annual Book of Standards, Part 31, D3694–78. ‘‘Standard Practices for Prepa- ration of Sample Containers and for Preser- vation of Organic Constituents,’’ American Society for Testing and Materials, Philadel- phia.

- ‘‘Carcinogens—Working With Carcino- gens,’’ Department of Health, Education, and Welfare, Public Health Service, Center for Disease Control, National Institute for Occu- pational Safety and Health, Publication No. 77–206, August 1977.

- ‘‘OSHA Safety and Health Standards, General Industry,’’ (29 CFR part 1910), Occu- pational Safety and Health Administration, OSHA 2206 (Revised, January 1976).

- ‘‘Safety in Academic Chemistry Labora- tories,’’American Chemical Society Publica- tion, Committee on Chemical Safety, 3rd Edition, 1979.

- Provost,  L.P.,  and  Elder,  R.S.  ‘‘Interpre- tation   of   Percent   Recovery   Data,’’   American Laboratory, 15, 58–63 (1983). (The value 2.44 used  in  the  equation  in  Section  8.3.3  is  two times the value 1.22 derived in this report.)

- ASTM Annual Book of Standards, Part 31, D3370–76. ‘‘Standard Practices for Sam- pling Water,’’ American Society for Testing and  Materials,  Philadelphia.

#### 40 CFR Ch. I (7–1–17 Edition)

- ‘‘Methods 330.4 (Titrimetric, DPD-FAS) and 330.5 (Spectrophotometric, DPD) for Chlorine, Total Residual,’’ Methods for Chemical Analysis of Water and Wastes, EPA–600/4–79–020, U.S. Environmental Pro- tection Agency, Environmental Monitoring and Support Laboratory, Cincinnati, Ohio 45268, March 1979.

- Eichelberger, J.W., Harris, L.E., and Budde, W.L. ‘‘Reference Compound to  Cali- brate Ion Abundance Measurement in Gas Chromatography-Mass Spectometry,’’ Ana- lytical Chemistry, 47, 995 (1975).

- McNair, N.M. and  Bonelli, E.J. ‘‘Basic Chromatography,’’ Consolidated Printing, Berkeley, California, p. 52, 1969.

- Burke, J.A. ‘‘Gas Chromatography for Pesticide Residue Analysis; Some Practical Aspects,’’ Journal of the Association of Official Analytical Chemists, 48, 1037 (1965).

- Olynyk, P., Budde, W.L., and Eichelberger, J.W. ‘‘Method Detection Limit for Methods 624 and 625,’’ Unpublished report, May 14, 1980.

- ‘‘EPA Method Study 30, Method 625, Base/Neutrals, Acids, and Pesticides,’’ EPA 600/4–84–053, National Technical Information Service, PB84–206572, Springfield, Virginia 22161, June 1984.

| Parameter | STORET No. | CAS No. |
| --- | --- | --- |
| Acenaphthene ................................. | 34205 | 83–32–9 |
| Acenaphthylene .............................. | 34200 | 208–96–8 |
| Anthracene ...................................... | 34220 | 120–12–7 |
| Aldrin ............................................... | 39330 | 309–00–2 |
| Benzo(a)anthracene ....................... | 34526 | 56–55–3 |
| Benzo(b)fluoranthene ...................... | 34230 | 205–99–2 |
| Benzo(k)fluoranthene ...................... | 34242 | 207–08–9 |
| Benzo(a)pyrene ............................... | 34247 | 50–32–8 |
| Benzo(ghi)perylene ......................... | 34521 | 191–24–2 |
| Benzyl butyl phthalate ..................... | 34292 | 85–68–7 |
| b-BHC ............................................. | 39338 | 319–85–7 |
| d-BHC .............................................. | 34259 | 319–86–8 |
| Bis(2-chloroethyl) ether ................... | 34273 | 111–44–4 |
| Bis(2-chloroethoxy)methane ........... | 34278 | 111–91–1 |
| Bis(2-ethylhexyl) phthalate .............. | 39100 | 117–81–7 |
| Bis(2-chloroisopropyl) ether a .......... | 34283 | 108–60–1 |
| 4-Bromophenyl phenyl ether a ........ | 34636 | 101–55–3 |
| Chlordane ........................................ | 39350 | 57–74–9 |
| 2-Chloronaphthalele ........................ | 34581 | 91–58–7 |
| 4-Chlorophenyl phenyl ether ........... | 34641 | 7005–72–3 |
| Chrysene ......................................... | 34320 | 218–01–9 |
| 4,4-DDD ......................................... | 39310 | 72–54–8 |
| 4,4-DDE ......................................... | 39320 | 72–55–9 |
| 4,4-DDT .......................................... | 39300 | 50–29–3 |
| Dibenzo(a,h)anthracene .................. | 34556 | 53–70–3 |
| Di-n-butylphthalate .......................... | 39110 | 84–74–2 |
| 1,3-Dichlorobenzene ....................... | 34566 | 541–73–1 |
| 1,2-Dichlorobenzene ....................... | 34536 | 95–50–1 |
| 1,4-Dichlorobenzene ....................... | 34571 | 106–46–7 |
| 3,3-Dichlorobenzidine .................... | 34631 | 91–94–1 |
| Dieldrin ............................................ | 39380 | 60–57–1 |
| Diethyl phthalate ............................. | 34336 | 84–66–2 |
| Dimethyl phthalate .......................... | 34341 | 131–11–3 |
| 2,4-Dinitrotoluene ............................ | 34611 | 121–14–2 |
| 2,6-Dinitrotoluene ............................ | 34626 | 606–20–2 |
| Di-n-octylphthalate .......................... | 34596 | 117–84–0 |
| Endosulfan sulfate .......................... | 34351 | 1031–07–8 |

TABLE 1—BASE/NEUTRAL EXTRACTABLES

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 625

TABLE 1—BASE/NEUTRAL EXTRACTABLES—

Continued

| Parameter | STORET No. | CAS No. |
| --- | --- | --- |
| 4-Chloro-3-methylphenol ................. | 34452 | 59–50–7 |
| 2-Chlorophenol ................................ | 34586 | 95–57–8 |
| 2,4-Dichlorophenol .......................... | 34601 | 120–83–2 |
| 2,4-Dimethylphenol ......................... | 34606 | 105–67–9 |
| 2,4-Dinitrophenol ............................. | 34616 | 51–28–5 |
| 2-Methyl-4,6-dinitrophenol .............. | 34657 | 534–52–1 |
| 2-Nitrophenol ................................... | 34591 | 88–75–5 |
| 4-Nitrophenol ................................... | 34646 | 100–02–7 |
| Pentachlorophenol .......................... | 39032 | 87–86–5 |
| Phenol ............................................. | 34694 | 108–95–2 |
| 2,4,6-Trichlorophenol ...................... | 34621 | 88–06–2 |

TABLE 2—ACID EXTRACTABLES

| Parameter | STORET No. | CAS No. |
| --- | --- | --- |
| Endrin aldehyde .............................. | 34366 | 7421–93–4 |
| Fluoranthene ................................... | 34376 | 206–44–0 |
| Fluorene .......................................... | 34381 | 86–73–7 |
| Heptachlor ....................................... | 39410 | 76–44–8 |
| Heptchlor epoxide ........................... | 39420 | 1024–57–3 |
| Hexachlorobenzene ........................ | 39700 | 118–74–1 |
| Hexachlorobutadiene ...................... | 34391 | 87–68–3 |
| Hexachloroethane ........................... | 34396 | 67–72–1 |
| Indeno(1,2,3-cd)pyrene ................... | 34403 | 193–39–5 |
| Isophorone ...................................... | 34408 | 78–59–1 |
| Naphthalene .................................... | 34696 | 91–20–3 |
| Nitrobenzene ................................... | 34447 | 98–95–3 |
| N-Nitrosodi-n-propylamine .............. | 34428 | 621–64–7 |
| PCB-1016 ........................................ | 34671 | 12674–11–2 |
| PCB-1221 ........................................ | 39488 | 11104–28–2 |
| PCB-1232 ........................................ | 39492 | 11141–16–5 |
| PCB-1242 ........................................ | 39496 | 53469–21–9 |
| PCB-1248 ........................................ | 39500 | 12672–29–6 |
| PCB-1254 ........................................ | 39504 | 11097–69–1 |
| PCB-1260 ........................................ | 39508 | 11096–82–5 |
| Phenanthrene ................................. | 34461 | 85–01–8 |
| Pyrene ............................................. | 34469 | 129–00–0 |
| Toxaphene ...................................... | 39400 | 8001–35–2 |
| 1,2,4-Trichlorobenzene ................... | 34551 | 120–82–1 |
| Parameter | STORET No. | CAS No. | Meth- od |
| Benzidine .......................... | 39120 | 92–87–5 | 605 |
| b-BHC ............................... | 39337 | 319–84–6 | 608 |
| d-BHC ............................... | 39340 | 58–89–8 | 608 |
| Endosulfan I ...................... | 34361 | 959–98–8 | 608 |
| Endosulfan II ..................... | 34356 | 33213–65–9 | 608 |
| Endrin ................................ | 39390 | 72–20–8 | 608 |
| Hexachlorocylopentadiene | 34386 | 77–47–4 | 612 |
| N-Nitrosodimethylamine .... | 34438 | 62–75–9 | 607 |
| N-Nitrosodiphenylamine .... | 34433 | 86–30–6 | 607 |

TABLE 3—ADDITIONAL EXTRACTABLE PARAMETERS A

a The	proper	chemical	name	is	2,2-oxybis(1- chloropropane).

a See Section 1.2.

TABLE 4—CHROMATOGRAPHIC CONDITIONS, METHOD DETECTION LIMITS, AND CHARACTERISTIC MASSES FOR BASE/NEUTRAL EXTRACTABLES

| Parameter | Reten- tion time (min) | Method detec- tion limit (g/L) | Characteristic masses |
| --- | --- | --- | --- |
|  |  |  | Electron impact | Chemical ionization |
|  |  |  | Primary | Sec- ondary | Sec- ondary |  |
|  |  |  |  |  |  | Methane | Methane | Methane |
| 1,3-Dichlorobenzene ............................. | 7.4 | 1.9 | 146 | 148 | 113 | 146 | 148 | 150 |
| 1,4-Dichlorobenzene ............................. | 7.8 | 4.4 | 146 | 148 | 113 | 146 | 148 | 150 |
| Hexachloroethane ................................. | 8.4 | 1.6 | 117 | 201 | 199 | 199 | 201 | 203 |
| Bis(2-chloroethyl) ether a ....................... | 8.4 | 5.7 | 93 | 63 | 95 | 63 | 107 | 109 |
| 1,2-Dichlorobenzene ............................. | 8.4 | 1.9 | 146 | 148 | 113 | 146 | 148 | 150 |
| Bis(2-chloroisopropyl) ether a ................ | 9.3 | 5.7 | 45 | 77 | 79 | 77 | 135 | 137 |
| N-Nitrosodi-n-propylamine .................... | .............. | .............. | 130 | 42 | 101 |  |  |  |
| Nitrobenzene ......................................... | 11.1 | 1.9 | 77 | 123 | 65 | 124 | 152 | 164 |
| Hexachlorobutadiene ............................ | 11.4 | 0.9 | 225 | 223 | 227 | 223 | 225 | 227 |
| 1,2,4-Trichlorobenzene ......................... | 11.6 | 1.9 | 180 | 182 | 145 | 181 | 183 | 209 |
| Isophorone ............................................ | 11.9 | 2.2 | 82 | 95 | 138 | 139 | 167 | 178 |
| Naphthalene .......................................... | 12.1 | 1.6 | 128 | 129 | 127 | 129 | 157 | 169 |
| Bis(2-chloroethoxy) methane ................ | 12.2 | 5.3 | 93 | 95 | 123 | 65 | 107 | 137 |
| Hexachlorocyclopentadiene a ................ | 13.9 | .............. | 237 | 235 | 272 | 235 | 237 | 239 |
| 2-Chloronaphthalene ............................. | 15.9 | 1.9 | 162 | 164 | 127 | 163 | 191 | 203 |
| Acenaphthylene .................................... | 17.4 | 3.5 | 152 | 151 | 153 | 152 | 153 | 181 |
| Acenaphthene ....................................... | 17.8 | 1.9 | 154 | 153 | 152 | 154 | 155 | 183 |
| Dimethyl phthalate ................................ | 18.3 | 1.6 | 163 | 194 | 164 | 151 | 163 | 164 |
| 2,6-Dinitrotoluene .................................. | 18.7 | 1.9 | 165 | 89 | 121 | 183 | 211 | 223 |
| Fluorene ................................................ | 19.5 | 1.9 | 166 | 165 | 167 | 166 | 167 | 195 |
| 4-Chlorophenyl phenyl ether ................. | 19.5 | 4.2 | 204 | 206 | 141 |  |  |  |
| 2,4-Dinitrotoluene .................................. | 19.8 | 5.7 | 165 | 63 | 182 | 183 | 211 | 223 |
| Diethyl phthalate ................................... | 20.1 | 1.9 | 149 | 177 | 150 | 177 | 223 | 251 |
| N-Nitrosodiphenylamine b ...................... | 20.5 | 1.9 | 169 | 168 | 167 | 169 | 170 | 198 |
| Hexachlorobenzene .............................. | 21.0 | 1.9 | 284 | 142 | 249 | 284 | 286 | 288 |
| b-BHC b ................................................. | 21.1 | .............. | 183 | 181 | 109 |  |  |  |
| 4-Bromophenyl phenyl ether ................. | 21.2 | 1.9 | 248 | 250 | 141 | 249 | 251 | 277 |
| d-BHC b ................................................. | 22.4 | .............. | 183 | 181 | 109 |  |  |  |
| Phenanthrene ........................................ | 22.8 | 5.4 | 178 | 179 | 176 | 178 | 179 | 207 |
| Anthracene ............................................ | 22.8 | 1.9 | 178 | 179 | 176 | 178 | 179 | 207 |
| b-BHC ................................................... | 23.4 | 4.2 | 181 | 183 | 109 |  |  |  |

#### Pt. 136, App. A, Meth. 625

40 CFR Ch. I (7–1–17 Edition)

TABLE 4—CHROMATOGRAPHIC CONDITIONS, METHOD DETECTION LIMITS, AND CHARACTERISTIC MASSES FOR BASE/NEUTRAL EXTRACTABLES—Continued

| Parameter | Reten- tion time (min) | Method detec- tion limit (g/L) | Characteristic masses |
| --- | --- | --- | --- |
|  |  |  | Electron impact | Chemical ionization |
|  |  |  | Primary | Sec- ondary | Sec- ondary |  |
|  |  |  |  |  |  | Methane | Methane | Methane |
| Heptachlor ............................................. | 23.4 | 1.9 | 100 | 272 | 274 | 149 | 205 | 279 |
| d-BHC .................................................... | 23.7 | 3.1 | 183 | 109 | 181 |  |  |  |
| Aldrin ..................................................... | 24.0 | 1.9 | 66 | 263 | 220 |  |  |  |
| Dibutyl phthalate ................................... | 24.7 | 2.5 | 149 | 150 | 104 |  |  |  |
| Heptachlor epoxide ............................... | 25.6 | 2.2 | 353 | 355 | 351 |  |  |  |
| Endosulfan I b ........................................ | 26.4 | .............. | 237 | 339 | 341 |  |  |  |
| Fluoranthene ......................................... | 26.5 | 2.2 | 202 | 101 | 100 | 203 | 231 | 243 |
| Dieldrin .................................................. | 27.2 | 2.5 | 79 | 263 | 279 |  |  |  |
| 4,4-DDE ................................................ | 27.2 | 5.6 | 246 | 248 | 176 |  |  |  |
| Pyrene ................................................... | 27.3 | 1.9 | 202 | 101 | 100 | 203 | 231 | 243 |
| Endrin b .................................................. | 27.9 | .............. | 81 | 263 | 82 |  |  |  |
| Endosulfan II b ....................................... | 28.6 | .............. | 237 | 339 | 341 |  |  |  |
| 4,4-DDD ............................................... | 28.6 | 2.8 | 235 | 237 | 165 |  |  |  |
| Benzidine b ............................................ | 28.8 | 44 | 184 | 92 | 185 | 185 | 213 | 225 |
| 4,4-DDT ................................................ | 29.3 | 4.7 | 235 | 237 | 165 |  |  |  |
| Endosulfan sulfate ................................ | 29.8 | 5.6 | 272 | 387 | 422 |  |  |  |
| Endrin aldehyde .................................... | .............. | .............. | 67 | 345 | 250 |  |  |  |
| Butyl benzyl phthalate ........................... | 29.9 | 2.5 | 149 | 91 | 206 | 149 | 299 | 327 |
| Bis(2-ethylhexyl) phthalate .................... | 30.6 | 2.5 | 149 | 167 | 279 | 149 |  |  |
| Chrysene ............................................... | 31.5 | 2.5 | 228 | 226 | 229 | 228 | 229 | 257 |
| Benzo(a)anthracene .............................. | 31.5 | 7.8 | 228 | 229 | 226 | 228 | 229 | 257 |
| 3,3-Dichlorobenzidine ........................... | 32.2 | 16.5 | 252 | 254 | 126 |  |  |  |
| Di-n-octyl phthalate ............................... | 32.5 | 2.5 | 149 |  |  |  |  |  |
| Benzo(b)fluoranthene ............................ | 34.9 | 4.8 | 252 | 253 | 125 | 252 | 253 | 281 |
| Benzo(k)fluoranthene ............................ | 34.9 | 2.5 | 252 | 253 | 125 | 252 | 253 | 281 |
| Benzo(a)pyrene ..................................... | 36.4 | 2.5 | 252 | 253 | 125 | 252 | 253 | 281 |
| Indeno(1,2,3-cd) pyrene ........................ | 42.7 | 3.7 | 276 | 138 | 277 | 276 | 277 | 305 |
| Dibenzo(a,h)anthracene ........................ | 43.2 | 2.5 | 278 | 139 | 279 | 278 | 279 | 307 |
| Benzo(ghi)perylene ............................... | 45.1 | 4.1 | 276 | 138 | 277 | 276 | 277 | 305 |
| N-Nitrosodimethylamine b ...................... | .............. | .............. | 42 | 74 | 44 |  |  |  |
| Chlordane c ............................................ | 19–30 | .............. | 373 | 375 | 377 |  |  |  |
| Toxaphene c .......................................... | 25–34 | .............. | 159 | 231 | 233 |  |  |  |
| PCB 1016 c ............................................ | 18–30 | .............. | 224 | 260 | 294 |  |  |  |
| PCB 1221 c ............................................ | 15–30 | 30 | 190 | 224 | 260 |  |  |  |
| PCB 1232 c ............................................ | 15–32 | .............. | 190 | 224 | 260 |  |  |  |
| PCB 1242 c ............................................ | 15–32 | .............. | 224 | 260 | 294 |  |  |  |
| PCB 1248 c ............................................ | 12–34 | .............. | 294 | 330 | 262 |  |  |  |
| PCB 1254 c ............................................ | 22–34 | 36 | 294 | 330 | 362 |  |  |  |
| PCB 1260 c ............................................ | 23–32 | .............. | 330 | 362 | 394 |  |  |  |

a The proper chemical name is 2,2-bisoxy(1-chloropropane).

b See Section 1.2.

c These compounds are mixtures of various isomers (See Figures 2 through 12). Column conditions: Supelcoport (100/120 mesh) coated with 3% SP–2250 packed in a 1.8 m long 2 mm ID glass column with helium carrier gas at 30 mL/min. flow rate. Column temperature held isothermal at 50 C for 4 min., then programmed at 8 C/min. to 270 C and held for 30 min.

TABLE 5—CHROMATOGRAPHIC CONDITIONS, METHOD DETECTION LIMITS, AND CHARACTERISTIC MASSES FOR ACID EXTRACTABLES

| Parameter | Reten- tion time (min) | Method detec- tion limit (g/L) | Characteristic masses |
| --- | --- | --- | --- |
|  |  |  | Electron Impact | Chemical ionization |
|  |  |  | Primary | Sec- ondary | Sec- ondary |  |
|  |  |  |  |  |  | Methane | Methane | Methane |
| 2-Chlorophenol ...................................... 2-Nitrophenol ......................................... Phenol ................................................... 2,4-Dimethylphenol ............................... 2,4-Dichlorophenol ................................ 2,4,6-Trichlorophenol ............................ 4-Chloro-3-methylphenol ....................... 2,4-Dinitrophenol ................................... 2-Methyl-4,6-dinitrophenol .................... Pentachlorophenol ................................ | 5.9 6.5 8.0 9.4 9.8 11.8 13.2 15.9 16.2 17.5 | 3.3 3.6 1.5 2.7 2.7 2.7 3.0 42 24 3.6 | 128 139 94 122 162 196 142 184 198 266 | 64 65 65 107 164 198 107 63 182 264 | 130 109 66 121 98 200 144 154 77 268 | 129 140 95 123 163 197 143 185 199 267 | 131 168 123 151 165 199 171 213 227 265 | 157 122 135 163 167 201 183 225 239 269 |

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 625

TABLE 5—CHROMATOGRAPHIC CONDITIONS, METHOD DETECTION LIMITS, AND CHARACTERISTIC MASSES FOR ACID EXTRACTABLES—Continued

| Parameter | Reten- tion time (min) | Method detec- tion limit (g/L) | Characteristic masses |
| --- | --- | --- | --- |
|  |  |  | Electron Impact | Chemical ionization |
|  |  |  | Primary | Sec- ondary | Sec- ondary |  |
|  |  |  |  |  |  | Methane | Methane | Methane |
| 4-Nitrophenol ......................................... | 20.3 | 2.4 | 65 | 139 | 109 | 140 | 168 | 122 |

Column conditions: Supelcoport (100/120 mesh) coated with 1% SP–1240DA packed in a 1.8 m long 2mm ID glass column with helium carrier gas at 30 mL/min. flow rate. Column temperature held isothermal at 70 C for 2 min. then programmed at 8

C/min. to 200 C.

TABLE 6—QC ACCEPTANCE CRITERIA—METHOD 625

| Parameter | Test conclu- sion (g/L) | Limits for s (g/L) | Range for X(g/L) | Range for P, Ps (Per- cent) |
| --- | --- | --- | --- | --- |
| Acenaphthene ....................................................................................... | 100 | 27.6 | 60.1–132.3 | 47–145 |
| Acenaphthylene ..................................................................................... | 100 | 40.2 | 53.5–126.0 | 33–145 |
| Aldrin ..................................................................................................... | 100 | 39.0 | 7.2–152.2 | D–166 |
| Anthracene ............................................................................................ | 100 | 32.0 | 43.4–118.0 | 27–133 |
| Benzo(a)anthracene .............................................................................. | 100 | 27.6 | 41.8–133.0 | 33–143 |
| Benzo(b)fluoranthene ............................................................................ | 100 | 38.8 | 42.0–140.4 | 24–159 |
| Benzo(k)fluoranthene ............................................................................ | 100 | 32.3 | 25.2–145.7 | 11–162 |
| Benzo(a)pyrene ..................................................................................... | 100 | 39.0 | 31.7–148.0 | 17–163 |
| Benzo(ghi)perylene ............................................................................... | 100 | 58.9 | D–195.0 | D–219 |
| Benzyl butyl phthalate ........................................................................... | 100 | 23.4 | D–139.9 | D–152 |
| b-BHC .................................................................................................... | 100 | 31.5 | 41.5–130.6 | 24–149 |
| d-BHC .................................................................................................... | 100 | 21.6 | D–100.0 | D–110 |
| Bis(2-chloroethyl) ether ......................................................................... | 100 | 55.0 | 42.9–126.0 | 12–158 |
| Bis(2-chloroethoxy)methane ................................................................. | 100 | 34.5 | 49.2–164.7 | 33–184 |
| Bis(2-chloroisopropyl) ether a ................................................................ | 100 | 46.3 | 62.8–138.6 | 36–166 |
| Bis(2-ethylhexyl) phthalate .................................................................... | 100 | 41.1 | 28.9–136.8 | 8–158 |
| 4-Bromophenyl phenyl ether ................................................................. | 100 | 23.0 | 64.9–114.4 | 53–127 |
| 2-Chloronaphthalene ............................................................................. | 100 | 13.0 | 64.5–113.5 | 60–118 |
| 4-Chlorophenyl phenyl ether ................................................................. | 100 | 33.4 | 38.4–144.7 | 25–158 |
| Chrysene ............................................................................................... | 100 | 48.3 | 44.1–139.9 | 17–168 |
| 4,4-DDD ................................................................................................ | 100 | 31.0 | D–134.5 | D–145 |
| 4,4-DDE ................................................................................................ | 100 | 32.0 | 19.2–119.7 | 4–136 |
| 4,4-DDT ................................................................................................ | 100 | 61.6 | D–170.6 | D–203 |
| Dibenzo(a,h)anthracene ........................................................................ | 100 | 70.0 | D–199.7 | D–227 |
| Di-n-butyl phthalate ............................................................................... | 100 | 16.7 | 8.4–111.0 | 1–118 |
| 1,2-Dichlorobenzene ............................................................................. | 100 | 30.9 | 48.6–112.0 | 32–129 |
| 1,3-Dichlorobenzene ............................................................................. | 100 | 41.7 | 16.7–153.9 | D–172 |
| 1,4,-Dichlorobenzene ............................................................................ | 100 | 32.1 | 37.3–105.7 | 20–124 |
| 3,3-Dhlorobenzidine ............................................................................. | 100 | 71.4 | 8.2–212.5 | D–262 |
| Dieldrin .................................................................................................. | 100 | 30.7 | 44.3–119.3 | 29–136 |
| Diethyl phthalate ................................................................................... | 100 | 26.5 | D–100.0 | D–114 |
| Dimethyl phthalate ................................................................................ | 100 | 23.2 | D–100.0 | D–112 |
| 2,4-Dinitrotoluene .................................................................................. | 100 | 21.8 | 47.5–126.9 | 39–139 |
| 2,6-Dinitrotoluene .................................................................................. | 100 | 29.6 | 68.1–136.7 | 50–158 |
| Di-n-octyl phthalate ............................................................................... | 100 | 31.4 | 18.6–131.8 | 4–146 |
| Endosulfan sulfate ................................................................................. | 100 | 16.7 | D–103.5 | D–107 |
| Endrin aldehyde .................................................................................... | 100 | 32.5 | D–188.8 | D–209 |
| Fluoranthene ......................................................................................... | 100 | 32.8 | 42.9–121.3 | 26–137 |
| Fluorene ................................................................................................ | 100 | 20.7 | 71.6–108.4 | 59–121 |
| Heptachlor ............................................................................................. | 100 | 37.2 | D–172.2 | D–192 |
| Heptachlor epoxide ............................................................................... | 100 | 54.7 | 70.9–109.4 | 26–155 |
| Hexachlorobenzene .............................................................................. | 100 | 24.9 | 7.8–141.5 | D–152 |
| Hexachlorobutadiene ............................................................................ | 100 | 26.3 | 37.8–102.2 | 24–116 |
| Hexachloroethane ................................................................................. | 100 | 24.5 | 55.2–100.0 | 40–113 |
| Indeno(1,2,3-cd)pyrene ......................................................................... | 100 | 44.6 | D–150.9 | D–171 |
| Isophorone ............................................................................................ | 100 | 63.3 | 46.6–180.2 | 21–196 |
| Naphthalene .......................................................................................... | 100 | 30.1 | 35.6–119.6 | 21–133 |
| Nitrobenzene ......................................................................................... | 100 | 39.3 | 54.3–157.6 | 35–180 |
| N-Nitrosodi-n-propylamine .................................................................... | 100 | 55.4 | 13.6–197.9 | D–230 |
| PCB-1260 .............................................................................................. | 100 | 54.2 | 19.3–121.0 | D–164 |
| Phenanthrene ........................................................................................ | 100 | 20.6 | 65.2–108.7 | 54–120 |
| Pyrene ................................................................................................... | 100 | 25.2 | 69.6–100.0 | 52–115 |
| 1,2,4-Trichlorobenzene ......................................................................... | 100 | 28.1 | 57.3–129.2 | 44–142 |
| 4-Chloro-3-methylphenol ....................................................................... | 100 | 37.2 | 40.8–127.9 | 22–147 |
| 2-Chlorophenol ...................................................................................... | 100 | 28.7 | 36.2–120.4 | 23–134 |

#### Pt. 136, App. A, Meth. 625

40 CFR Ch. I (7–1–17 Edition)

TABLE 6—QC ACCEPTANCE CRITERIA—METHOD 625—Continued

| Parameter | Test conclu- sion (g/L) | Limits for s (g/L) | Range for X(g/L) | Range for P, Ps (Per- cent) |
| --- | --- | --- | --- | --- |
| 2,4-Dichlorophenol ................................................................................ | 100 | 26.4 | 52.5–121.7 | 39–135 |
| 2,4-Dimethylphenol ............................................................................... | 100 | 26.1 | 41.8–109.0 | 32–119 |
| 2,4-Dinitrophenol ................................................................................... | 100 | 49.8 | D–172.9 | D–191 |
| 2-Methyl-4,6-dinitrophenol ..................................................................... | 100 | 93.2 | 53.0–100.0 | D–181 |
| 2-Nitrophenol ......................................................................................... | 100 | 35.2 | 45.0–166.7 | 29–182 |
| 4-Nitrophenol ......................................................................................... | 100 | 47.2 | 13.0–106.5 | D–132 |
| Pentachlorophenol ................................................................................ | 100 | 48.9 | 38.1–151.8 | 14–176 |
| Phenol ................................................................................................... | 100 | 22.6 | 16.6–100.0 | 5–112 |
| 2,4,6-Trichlorophenol ............................................................................ | 100 | 31.7 | 52.4–129.2 | 37–144 |

s = Standard deviation for four recovery measurements, in g/L (Section 8.2.4). X¯ = Average recovery for four recovery measurements, in g/L (Section 8.2.4).

P, Ps  = Percent recovery measured (Section 8.3.2, Section 8.4.2). D = Detected; result must be greater than zero.

NOTE: These criteria are based directly upon the method performance data in Table 7. Where necessary, the limits for recov- ery have been broadened to assure applicability of the limts to concentrations below those used to develop Table 7.

a The proper chemical name is 2,2oxybis(1-chloropropane).

TABLE 7—METHOD ACCURACY AND PRECISION AS FUNCTIONS OF CONCENTRATION—METHOD 625

| Parameter | Accuracy, as recovery, X (g/L) | Single analyst precision, sr’ (g/L) | Overall preci- sion, S(g/L) |
| --- | --- | --- | --- |
| Acenaphthene ................................................................................................... | 0.96C = 0.19 | 0.15X¯ ¥0.12 | 0.21X¯ ¥0.67 |
| Acenaphthylene ................................................................................................. | 0.89C = 0.74 | 0.24X¯ ¥1.06 | 0.26X¯ ¥0.54 |
| Aldrin ................................................................................................................. | 0.78C = 1.66 | 0.27X¯ ¥1.28 | 0.43X¯ = 1.13 |
| Anthracene ........................................................................................................ | 0.80C = 0.68 | 0.21X¯ ¥0.32 | 0.27X¯ ¥0.64 |
| Benzo(a)anthracene .......................................................................................... | 0.88C¥0.60 | 0.15X¯ = 0.93 | 0.26X¯ ¥0.28 |
| Benzo(b)fluoranthene ........................................................................................ | 0.93C¥1.80 | 0.22X¯ = 0.43 | 0.29X¯ = 0.96 |
| Benzo(k)fluoranthene ........................................................................................ | 0.87C¥1.56 | 0.19X¯ = 1.03 | 0.35X¯ = 0.40 |
| Benzo(a)pyrene ................................................................................................. | 0.90C¥0.13 | 0.22X¯ = 0.48 | 0.32X¯ = 1.35 |
| Benzo(ghi)perylene ........................................................................................... | 0.98C¥0.86 | 0.29X¯ = 2.40 | 0.51X¯ ¥0.44 |
| Benzyl butyl phthalate ....................................................................................... | 0.66C¥1.68 | 0.18X¯ = 0.94 | 0.53X¯ = 0.92 |
| b-BHC ................................................................................................................ | 0.87C¥0.94 | 0.20X¯ ¥0.58 | 0.30X¯ ¥1.94 |
| d-BHC ................................................................................................................ | 0.29C¥1.09 | 0.34X¯ = 0.86 | 0.93X¯ ¥0.17 |
| Bis(2-chloroethyl) ether ..................................................................................... | 0.86C¥1.54 | 0.35X¯ ¥0.99 | 0.35X¯ = 0.10 |
| Bis(2-chloroethoxy)methane .............................................................................. | 1.12C¥5.04 | 0.16X¯ = 1.34 | 0.26X¯ = 2.01 |
| Bis(2-chloroisopropyl) ether a ............................................................................ | 1.03C¥2.31 | 0.24X¯ = 0.28 | 0.25X¯ = 1.04 |
| Bis(2-ethylhexyl) phthalate ................................................................................ | 0.84C¥1.18 | 0.26X¯ = 0.73 | 0.36X¯ = 0.67 |
| 4-Bromophenyl phenyl ether ............................................................................. | 0.91C¥1.34 | 0.13X¯ = 0.66 | 0.16X¯ = 0.66 |
| 2-Chloronaphthalene ......................................................................................... | 0.89C = 0.01 | 0.07X¯ = 0.52 | 0.13X¯ = 0.34 |
| 4-Chlorophenyl phenyl ether ............................................................................. | 0.91C = 0.53 | 0.20X¯ ¥0.94 | 0.30X¯ ¥0.46 |
| Chrysene ........................................................................................................... | 0.93C¥1.00 | 0.28X¯ = 0.13 | 0.33X¯ ¥0.09 |
| 4,4-DDD ............................................................................................................ | 0.56C¥0.40 | 0.29X¯ ¥0.32 | 0.66X¯ ¥0.96 |
| 4,4-DDE ............................................................................................................ | 0.70C¥0.54 | 0.26X¯ ¥1.17 | 0.39X¯ ¥1.04 |
| 4,4-DDT ............................................................................................................ | 0.79C¥3.28 | 0.42X¯ = 0.19 | 0.65X¯ ¥0.58 |
| Dibenzo(a,h)anthracene .................................................................................... | 0.88C = 4.72 | 0.30X¯ = 8.51 | 0.59X¯ = 0.25 |
| Di-n-butyl phthalate ........................................................................................... | 0.59C = 0.71 | 0.13X¯ = 1.16 | 0.39X¯ = 0.60 |
| 1,2-Dichlorobenzene ......................................................................................... | 0.80C = 0.28 | 0.20X¯ = 0.47 | 0.24X¯ = 0.39 |
| 1,3-Dichlorobenzene ......................................................................................... | 0.86C¥0.70 | 0.25X¯ = 0.68 | 0.41X¯ = 0.11 |
| 1,4-Dichlorobenzene ......................................................................................... | 0.73C¥1.47 | 0.24X¯ = 0.23 | 0.29X¯ = 0.36 |
| 3,3-Dichlorobenzidine ....................................................................................... | 1.23C¥12.65 | 0.28X¯ = 7.33 | 0.47X¯ = 3.45 |
| Dieldrin .............................................................................................................. | 0.82C¥0.16 | 0.20X¯ ¥0.16 | 0.26X¯ ¥0.07 |
| Diethyl phthalate ................................................................................................ | 0.43C = 1.00 | 0.28X¯ = 1.44 | 0.52X¯ = 0.22 |
| Dimethyl phthalate ............................................................................................. | 0.20C = 1.03 | 0.54X¯ = 0.19 | 1.05X¯ ¥0.92 |
| 2,4-Dinitrotoluene .............................................................................................. | 0.92C¥4.81 | 0.12X¯ = 1.06 | 0.21X¯ = 1.50 |
| 2,6-Dinitrotoluene .............................................................................................. | 1.06C¥3.60 | 0.14X¯ = 1.26 | 0.19X¯ = 0.35 |
| Di-n-octyl phthalate ........................................................................................... | 0.76C¥0.79 | 0.21X¯ = 1.19 | 0.37X¯ = 1.19 |
| Endosulfan sulfate ............................................................................................. | 0.39C = 0.41 | 0.12X¯ = 2.47 | 0.63X¯ ¥1.03 |
| Endrin aldehyde ................................................................................................ | 0.76C¥3.86 | 0.18X¯ = 3.91 | 0.73X¯ ¥0.62 |
| Fluoranthene ..................................................................................................... | 0.81C = 1.10 | 0.22X¯ ¥0.73 | 0.28X¯ ¥0.60 |
| Fluorene ............................................................................................................ | 0.90C¥0.00 | 0.12X¯ = 0.26 | 0.13X¯ = 0.61 |
| Heptachlor ......................................................................................................... | 0.87C¥2.97 | 0.24X¯ ¥0.56 | 0.50X¯ ¥0.23 |
| Heptachlor epoxide ........................................................................................... | 0.92C¥1.87 | 0.33X¯ ¥0.46 | 0.28X¯ = 0.64 |
| Hexachlorobenzene ........................................................................................... | 0.74C = 0.66 | 0.18X¯ ¥0.10 | 0.43X¯ ¥0.52 |
| Hexachlorobutadiene ......................................................................................... | 0.71C¥1.01 | 0.19X¯ = 0.92 | 0.26X¯ = 0.49 |
| Hexachloroethane ............................................................................................. | 0.73C¥0.83 | 0.17X¯ = 0.67 | 0.17X¯ = 0.80 |
| Indeno(1,2,3-cd)pyrene ..................................................................................... | 0.78C¥3.10 | 0.29X¯ = 1.46 | 0.50X¯ = 0.44 |
| Isophorone ......................................................................................................... | 1.12C = 1.41 | 0.27X¯ = 0.77 | 0.33X¯ = 0.26 |
| Naphthalene ...................................................................................................... | 0.76C = 1.58 | 0.21X¯ ¥0.41 | 0.30X¯ ¥0.68 |

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 625

TABLE 7—METHOD ACCURACY AND PRECISION AS FUNCTIONS OF CONCENTRATION—METHOD 625—

Continued

| Parameter | Accuracy, as recovery, X (g/L) | Single analyst precision, sr’ (g/L) | Overall preci- sion, S(g/L) |
| --- | --- | --- | --- |
| Nitrobenzene ..................................................................................................... | 1.09C¥3.05 | 0.19X¯ = 0.92 | 0.27X¯ = 0.21 |
| N-Nitrosodi-n-propylamine ................................................................................. | 1.12C¥6.22 | 0.27X¯ = 0.68 | 0.44X¯ = 0.47 |
| PCB–1260 ......................................................................................................... | 0.81C¥10.86 | 0.35X¯ = 3.61 | 0.43X¯ = 1.82 |
| Phenanthrene .................................................................................................... | 0.87C¥0.06 | 0.12X¯ = 0.57 | 0.15X¯ = 0.25 |
| Pyrene ............................................................................................................... | 0.84C¥0.16 | 0.16X¯ = 0.06 | 0.15X¯ = 0.31 |
| 1,2,4-Trichlorobenzene ...................................................................................... | 0.94C¥0.79 | 0.15X¯ = 0.85 | 0.21X¯ = 0.39 |
| 4-Chloro-3-methylphenol ................................................................................... | 0.84C = 0.35 | 0.23X¯ = 0.75 | 0.29X¯ = 1.31 |
| 2-Chlorophenol .................................................................................................. | 0.78C = 0.29 | 0.18X¯ = 1.46 | 0.28X¯ = 0.97 |
| 2,4-Dichlorophenol ............................................................................................ | 0.87C = 0.13 | 0.15X¯ = 1.25 | 0.21X¯ = 1.28 |
| 2,4-Dimethylphenol ............................................................................................ | 0.71C = 4.41 | 0.16X¯ = 1.21 | 0.22X¯ = 1.31 |
| 2,4-Dinitrophenol ............................................................................................... | 0.81C¥18.04 | 0.38X¯ = 2.36 | 0.42X¯ = 26.29 |
| 2-Methyl-4,6-Dinitrophenol ................................................................................ | 1.04C¥28.04 | 0.05X¯ = 42.29 | 0.26X¯ = 23.10 |
| 2-Nitrophenol ..................................................................................................... | 1.07C¥1.15 | 0.16X¯ = 1.94 | 0.27X¯ = 2.60 |
| 4-Nitrophenol ..................................................................................................... | 0.61C¥1.22 | 0.38X¯ = 2.57 | 0.44X¯ = 3.24 |
| Pentachlorophenol ............................................................................................. | 0.93C = 1.99 | 0.24X¯ = 3.03 | 0.30X¯ = 4.33 |
| Phenol ............................................................................................................... | 0.43C = 1.26 | 0.26X¯ = 0.73 | 0.35X¯ = 0.58 |
| 2,4,6-Trichlorophenol ......................................................................................... | 0.91C¥0.18 | 0.16X¯ = 2.22 | 0.22X¯ = 1.81 |

X= Expected recovery for one or more measurements of a sample containing a concentration of C, in g/L.

sr= Expected single analyst standard deviation of measurements at an average concentration found of X¯ , in g/L. S= Expected interlaboratory standard deviation of measurements at an average concentration found of X¯ , in g/L. C= True value for the concentration, in g/L.

X¯ = Average recovery found for measurements of samples containing a concentration of C, in g/L.

a The proper chemical name is 2,2oxybis(1-chloropropane).

TABLE 8—SUGGESTED INTERNAL AND

SURROGATE STANDARDS

TABLE 9—DFTPP KEY MASSES AND

ABUNDANCE CRITERIA

| Base/neutral fraction | Acid fraction |
| --- | --- |
| Aniline-d5 ................................ Anthracene-d10 ....................... Benzo(a)anthracene-d12 ......... 4,4-Dibromobiphenyl .............. 4,4- Dibromooctafluorobiphenyl. Decafluorobiphenyl. 2,2 1-Difluorobiphenyl. 4-Fluoroaniline. 1-Fluoronaphthalene. 2-Fluoronaphthalene. Naphthalene-d8. Nitrobenzene-d5. 2,3,4,5,6-Pentafluorobiphenyl. Phenanthrene-d10. Pyridine-d5 .............................. | 2-Fluorophenol. Pentafluorophenol. Phenol-d5 2-Perfluoromethyl phenol. |
| Mass | m/z Abundance criteria |
| 51 | 30–60 percent of mass 198. |
| 68 | Less than 2 percent of mass 69. |
| 70 | Less than 2 percent of mass 69. |
| 127 | 40–60 percent of mass 198. |
| 197 | Less than 1 percent of mass 198. |
| 198 | Base peak, 100 percent relative abundance. |
| 199 | 5–9 percent of mass 198. |
| 275 | 10–30 percent of mass 198. |
| 365 | Greater than 1 percent of mass 198. |
| 441 | Present but less than mass 443. |
| 442 | Greater than 40 percent of mass 198. |
| 443 | 17–23 percent of mass 442. |

#### Pt. 136, App. A, Meth. 625

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 625

Pt. 136, App. A, Meth. 625

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 625

Pt. 136, App. A, Meth. 625

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 625

Pt. 136, App. A, Meth. 625

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 625

Pt. 136, App. A, Meth. 625

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 625

Pt. 136, App. A, Meth. 625

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 625

Pt. 136, App. A, Meth. 625

40 CFR Ch. I (7–1–17 Edition)

ATTACHMENT 1 TO METHOD 625 INTRODUCTION

To     support     measurement     of     several

semivolatile pollutants, EPA has developed this attachment to EPA Method 625. 1 The modifications listed in this attachment are approved only for monitoring wastestreams from the Centralized Waste Treatment Point Source Category (40 CFR part 437) and the Landfills Point Source  Category  (40  CFR part 445). EPA Method 625 (the Method) in- volves sample extraction with methylene chloride followed by analysis of the extract using either packed or capillary column gas chromatography/mass spectrometry (GC/ MS). This attachment addresses the addition of the semivolatile pollutants listed in Ta- bles 1 and 2,  to  all  applicable  standard, stock, and spiking solutions utilized for the determination of semivolatile organic com- pounds by EPA Method 625.

1.0    EPA METHOD 625 MODIFICATION SUMMARY

The additional semivolatile organic com- pounds listed in Tables 1  and  2  are  added  to all applicable calibration, spiking, and other solutions utilized  in the  determination of base/neutral and acid compounds by EPA Method 625. The instrument is to  be  cali- brated with these compounds, using a cap- illary column, and all procedures and quality control tests stated in the Method must be performed.

2.0    SECTION MODIFICATIONS

NOTE: All section and figure numbers in this Attachment reference section and figure numbers in EPA Method 625 unless noted otherwise. Sections not listed here remain unchanged.

Section 6.7 The stock standard solutions de- scribed in this section are modified such that the analytes in Tables 1 and 2 of this attachment are required in addition to those  specified  in  the  Method.

Section 7.2 The calibration standards de- scribed in this section are modified to in- clude the analytes in Tables 1 and  2  of this    attachment.

Section 8.2 The precision and accuracy re- quirements are modified to include the analytes listed in Tables 1 and 2 of this attachment. Additional performance cri- teria are supplied in Table 5 of this at- tachment.

Section 8.3 The matrix spike is modified to include  the  analytes  listed  in  Tables  1 and  2  of  this  attachment.

Section 8.4 The QC  check  standard  is  modi- fied to include the analytes listed in Ta- bles 1 and 2  of  this  attachment.  Addi- tional  performance  criteria  are   supplied in  Table  5  of  this  attachment.

Section 16.0 Additional method perform- ance information is supplied with this at- tachment.

TABLE 1—BASE/NEUTRAL EXTRACTABLES

| Parameter | CAS No. |
| --- | --- |
| acetophenone 1 .................................................. | 98–86–2 |
| alpha-terpineol 3 ................................................. | 98–55–5 |
| aniline 2 .............................................................. | 62–53–3 |
| carbazole 1 ......................................................... | 86–74–8 |
| o-cresol 1 ............................................................ | 95–48–7 |
| n-decane 1 .......................................................... | 124–18–5 |
| 2,3-dichloroaniline 1 ........................................... | 608–27–5 |
| n-octadecane 1 ................................................... | 593–45–3 |
| pyridine 2 ............................................................ | 110–86–1 |

CAS = Chemical Abstracts Registry.

1 Analysis of this pollutant is approved only for the Central- ized Waste Treatment industry.

2 Analysis of this pollutant is approved only for the Central- ized Waste Treatment and Landfills industries.

3 Analysis of this pollutant is approved only for the Landfills industry.

TABLE 2—ACID EXTRACTABLES

| Parameter | CAS No. |
| --- | --- |
| p-cresol 1 ............................................................ | 106–44–5 |

CAS = Chemical Abstracts Registry.

1 Analysis of this pollutant is approved only for the Central- ized Waste Treatment and Landfills industries.

TABLE 3—CHROMATOGRAPHIC CONDITIONS, 1 METHOD DETECTION LIMITS (MDLS), AND

CHARACTERISTIC M/Z’S FOR BASE/NEUTRAL EXTRACTABLES

| Analyte | Retention time (min) 2 | MDL (g/L) | Characteristic m/z’s |
| --- | --- | --- | --- |
|  |  |  | Electron impact |
|  |  |  | Primary | Secondary | Secondary |
| pyridine 3 ........................................................................ | 4.93 | 4.6 | 79 | 52 | 51 |
| N-Nitro sodimethylamine ............................................... | 4.95 | .................... | 42 | 74 | 44 |
| aniline 3 .......................................................................... | 10.82 | 3.3 | 93 | 66 | 65 |
| Bis(2-chloroethyl)ether .................................................. | 10.94 | .................... | 93 | 63 | 95 |
| n-decane 4 ..................................................................... | 11.11 | 5.0 | 57 |  |  |
| 1,3-Dichlorobenzene ..................................................... | 11.47 | .................... | 146 | 148 | 113 |
| 1,4-Dichlorobenzene ..................................................... | 11.62 | .................... | 146 | 148 | 113 |
| 1,2-Dichlorobenzene ..................................................... | 12.17 | .................... | 146 | 148 | 113 |

1 EPA Method 625: Base/Neutrals and Acids, 40 CFR part 136, appendix A.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 625

TABLE 3—CHROMATOGRAPHIC CONDITIONS, 1 METHOD DETECTION LIMITS (MDLS), AND

CHARACTERISTIC M/Z’S FOR BASE/NEUTRAL EXTRACTABLES—Continued

| Analyte | Retention time (min) 2 | MDL (g/L) | Characteristic m/z’s |
| --- | --- | --- | --- |
|  |  |  | Electron impact |
|  |  |  | Primary | Secondary | Secondary |
| o-creso 1 ........................................................................ | 12.48 | 4.7 | 108 | 107 | 79 |
| Bis(2-chloro- isopropyl)ether ......................................... | 12.51 | .................... | 45 | 77 | 79 |
| acetophenone 4 ............................................................. | 12.88 | 3.4 | 105 | 77 | 51 |
| N-Nitrosodi-n-propylamine ............................................ | 12.97 | .................... | 130 | 42 | 101 |
| Hexachloroethane ......................................................... | 13.08 | .................... | 117 | 201 | 199 |
| Nitrobenzene ................................................................. | 13.40 | .................... | 77 | 123 | 65 |
| Isophorone .................................................................... | 14.11 | .................... | 82 | 95 | 138 |
| Bis (2-chloro ethoxy)methane ....................................... | 14.82 | .................... | 93 | 95 | 123 |
| 1,2,4-Trichlorobenzene ................................................. | 15.37 | .................... | 180 | 182 | 145 |
| alpha-terpineol ............................................................... | 15.55 | 5.0 | 59 |  |  |
| Naphthalene .................................................................. | 15.56 | .................... | 128 | 129 | 127 |
| Hexachlorobutadiene .................................................... | 16.12 | .................... | 225 | 223 | 227 |
| Hexachlorocyclopentadiene .......................................... | 18.47 | .................... | 237 | 235 | 272 |
| 2,3-dichloroaniline 4 ....................................................... | 18.82 | 2.5 | 161 | 163 | 90 |
| 2-Chloronaphthalene ..................................................... | 19.35 | .................... | 162 | 164 | 127 |
| Dimethyl phthalate ........................................................ | 20.48 | .................... | 163 | 194 | 164 |
| Acenaphthylene ............................................................. | 20.69 | .................... | 152 | 151 | 153 |
| 2,6-Dinitrotoluene .......................................................... | 20.73 | .................... | 165 | 89 | 121 |
| Acenaphthene ............................................................... | 21.30 | .................... | 154 | 153 | 152 |
| 2,4-Dinitrotoluene .......................................................... | 22.00 | .................... | 165 | 63 | 182 |
| Diethylphthalate ............................................................. | 22.74 | .................... | 149 | 177 | 150 |
| 4-Chlorophenyl phenyl ether ......................................... | 22.90 | .................... | 204 | 206 | 141 |
| Fluorene ........................................................................ | 22.92 | .................... | 166 | 165 | 167 |
| N-Nitro sodiphenylamine ............................................... | 23.35 | .................... | 169 | 168 | 167 |
| 4-Bromophenyl phenyl ether ......................................... | 24.44 | .................... | 248 | 250 | 141 |
| Hexachlorobenzene ...................................................... | 24.93 | .................... | 284 | 142 | 249 |
| n-octadecane 4 .............................................................. | 25.39 | 2.0 | 57 |  |  |
| Phenanthrene ................................................................ | 25.98 | .................... | 178 | 179 | 176 |
| Anthracene .................................................................... | 26.12 | .................... | 178 | 179 | 176 |
| Carbazole 4 .................................................................... | 26.66 | 4.0 | 167 |  |  |
| Dibutyl phthalate ........................................................... | 27.84 | .................... | 149 | 150 | 104 |
| Fluoranthene ................................................................. | 29.82 | .................... | 202 | 101 | 100 |
| Benzidine ....................................................................... | 30.26 | .................... | 184 | 92 | 185 |
| Pyrene ........................................................................... | 30.56 | .................... | 202 | 101 | 100 |
| Butyl benzyl phthalate ................................................... | 32.63 | .................... | 149 | 91 | 206 |
| 3,3-Dichlorobenzidine ................................................... | 34.28 | .................... | 252 | 254 | 126 |
| Benzo(a)anthracene ...................................................... | 34.33 | .................... | 228 | 229 | 226 |
| Bis(2-ethyl hexyl)phthalate ............................................ | 34.36 | .................... | 149 | 167 | 279 |
| Chrysene ....................................................................... | 34.44 | .................... | 228 | 226 | 229 |
| Di-n-octyl-phthalate ....................................................... | 36.17 | .................... | 149 |  |  |
| Benzo(b)fluoranthene .................................................... | 37.90 | .................... | 252 | 253 | 125 |
| Benzo(k)fluoranthene .................................................... | 37.97 | .................... | 252 | 253 | 125 |
| Benzo(a)pyrene ............................................................. | 39.17 | .................... | 252 | 253 | 125 |
| Dibenzo(a,h) anthracene ............................................... | 44.91 | .................... | 278 | 139 | 279 |
| Indeno(1,2,3-c,d)pyrene ................................................ | 45.01 | .................... | 276 | 138 | 277 |
| Benzo(ghi)perylene ....................................................... | 46.56 | .................... | 276 | 138 | 277 |

1 The data presented in this table were obtained under the following conditions:

Column—30 5 meters 0.25 .02 mm i.d., 94% methyl, 5% phenyl, 1% vinyl, bonded phase fused silica capillary column (DB–5).

Temperature program—Five minutes at 30 C; 30–280 C at 8 C per minute; isothermal at 280 C until benzo(ghi)perylene

elutes.

Gas velocity—30 5 cm/sec at 30 C.

2 Retention times are from Method 1625, Revision C, using a capillary column, and are intended to be consistent for all analytes in Tables 4 and 5 of this attachment.

3 Analysis of this pollutant is approved only for the Centralized Waste Treatment and Landfills industries.

4 Analysis of this pollutant is approved only for the Centralized Waste Treatment industry.

TABLE 4—CHROMATOGRAPHIC CONDITIONS, 1 METHOD DETECTION LIMITS (MDLS), AND

CHARACTERISTIC M/Z’S FOR ACID EXTRACTABLES

| Analyte | Retention time 2 (min) | MDL (g/L) | Characteristic m/z’s |
| --- | --- | --- | --- |
|  |  |  | Electron impact |
|  |  |  | Primary | Secondary | Secondary |
| Phenol ........................................................................... | 10.76 | .................... | 94 | 65 | 66 |
| 2-Chlorophenol .............................................................. | 11.08 | .................... | 128 | 64 | 130 |

#### Pt. 136, App. A, Meth. 1613

40 CFR Ch. I (7–1–17 Edition)

TABLE 4—CHROMATOGRAPHIC CONDITIONS, 1 METHOD DETECTION LIMITS (MDLS), AND

CHARACTERISTIC M/Z’S FOR ACID EXTRACTABLES—Continued

| Analyte | Retention time 2 (min) | MDL (g/L) | Characteristic m/z’s |
| --- | --- | --- | --- |
|  |  |  | Electron impact |
|  |  |  | Primary | Secondary | Secondary |
| p-cresol 3 ....................................................................... | 12.92 | 7.8 | 108 | 107 | 77 |
| 2-Nitrophenol ................................................................. | 14.38 | .................... | 139 | 65 | 109 |
| 2,4-Dimethylphenol ....................................................... | 14.54 | .................... | 122 | 107 | 121 |
| 2,4-Dichlorophenol ........................................................ | 15.12 | .................... | 162 | 164 | 98 |
| 4-Chloro-3-methylphenol ............................................... | 16.83 | .................... | 142 | 107 | 144 |
| 2,4,6-Trichlorophenol .................................................... | 18.80 | .................... | 196 | 198 | 200 |
| 2,4-Dinitrophenol ........................................................... | 21.51 | .................... | 184 | 63 | 154 |
| 4-Nitrophenol ................................................................. | 21.77 | .................... | 65 | 139 | 109 |
| 2-Methyl-4,6-dinitrophenol ............................................. | 22.83 | .................... | 198 | 182 | 77 |
| Pentachlorophenol ........................................................ | 25.52 | .................... | 266 | 264 | 268 |

1 The data presented in this table were obtained under the following conditions:

Column—30 5 meters 0.25 .02 mm i.d., 94% methyl, 5% phenyl, 1% vinyl silicone bonded phase fused silica capillary col- umn (DB–5).

Temperature program—Five minutes at 30 C; 30–280 C at 8 C per minute; isothermal at 280 C until benzo(ghi)perylene elutes.

Gas velocity—30 5 cm/sec at 30 C

2 Retention times are from EPA Method 1625, Revision C, using a capillary column, and are intended to be consistent for all analytes in Tables 3 and 4 of this attachment.

3 Analysis of this pollutant is approved only for the Centralized Waste Treatment and Landfills industries.

TABLE 5—QC ACCEPTANCE CRITERIA

| Analyte | Test conclu- sion (g/L) | Limits for s (g/L) | Range for X (g/L) | Range for P, Ps(%) |
| --- | --- | --- | --- | --- |
| acetophenone 1 ..................................................................................... | 100 | 51 | 23–254 | 61–144 |
| alpha-terpineol ....................................................................................... | 100 | 47 | 46–163 | 58–156 |
| aniline 2 .................................................................................................. | 100 | 71 | 15–278 | 46–134 |
| carbazole 1 ............................................................................................. | 100 | 17 | 79–111 | 73–131 |
| o-cresol 1 ............................................................................................... | 100 | 23 | 30–146 | 55–126 |
| p-cresol 2 ............................................................................................... | 100 | 22 | 11–617 | 76–107 |
| n-decane 1 ............................................................................................. | 100 | 70 | D–651 | D-ns |
| 2,3-dichloroaniline 1 ............................................................................... | 100 | 13 | 40–160 | 68–134 |
| n-octadecane 1 ...................................................................................... | 100 | 10 | 52–147 | 65–123 |
| pyridine 2 ................................................................................................ | 100 | ns | 7–392 | 33–158 |

s = Standard deviation for four recovery measurements, in g/L (Section 8.2) X = Average recovery for four recovery measurements in g/L (Section 8.2) P,Ps = Percent recovery measured (Section 8.3, Section 8.4)

D = Detected; result must be greater than zero.

ns = no specification; limit is outside the range that can be measured reliably.

1 Analysis of this pollutant is approved only for the Centralized Waste Treatment industry.

2 Analysis of this pollutant is approved only for the Centralized Waste Treatment and Landfills industries.

METHOD 1613, REVISION B

Tetra- Through Octa-Chlorinated Dioxins and Furans by Isotope Dilution HRGC/HRMS

1.0   Scope and Application

  - This method is for determination of tetra- through octa-chlorinated dibenzo-p- dioxins (CDDs) and dibenzofurans (CDFs) in water, soil, sediment, sludge, tissue, and other sample matrices by high resolution gas chromatography/high resolution mass spec- trometry (HRGC/HRMS). The method is for use in EPA’s data gathering and monitoring programs associated with the Clean Water Act, the Resource Conservation and Recov- ery Act, the Comprehensive Environmental Response, Compensation and  Liability  Act, and the Safe Drinking Water Act. The meth-

od is based on a compilation of EPA, indus- try, commercial laboratory, and academic methods (References 1–6).

  - The seventeen 2,3,7,8-substituted CDDs/CDFs listed in Table 1 may be deter- mined  by  this   method.   Specifications   are also provided for separate determination of 2,3,7,8-tetrachloro-dibenzo-p-dioxin (2,3,7,8- TCDD) and 2,3,7,8-tetrachloro-dibenzofuran (2,3,7,8-TCDF).

  - The detection limits and quantitation levels in this method are  usually  dependent on the level of interferences rather than in- strumental limitations. The minimum levels (MLs) in Table 2 are the levels at which the CDDs/CDFs can be determined with no inter- ferences    present.    The    Method    Detection

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1613

Limit (MDL) for 2,3,7,8-TCDD has been deter- mined as 4.4 pg/L (parts-per-quadrillion) using this method.

  - The GC/MS portions of this method are for use only by analysts experienced with HRGC/HRMS or under the  close  supervision of such qualified persons. Each laboratory that uses this method must demonstrate the ability to generate acceptable results using the procedure in Section 9.2.

  - This method is ‘‘performance-based’’. The analyst is permitted to modify the method to overcome interferences or lower the cost of measurements, provided that all performance criteria in this method are met. The requirements for establishing method equivalency are given in Section 9.1.2.

  - Any modification of this method,  be- yond those expressly permitted, shall be con- sidered a major modification subject to ap- plication and approval of alternate test pro- cedures under 40 CFR 136.4 and 136.5.

2.0   Summary of Method

Flow charts that summarize procedures for sample preparation, extraction, and analysis are given in Figure 1 for aqueous and solid samples, Figure 2 for multi-phase samples, and Figure 3 for tissue samples.

  - Extraction.

    - Aqueous samples  (samples  con- taining less  than  1%  solids)—Stable isotopically labeled analogs of 15 of the 2,3,7,8-substituted  CDDs/CDFs   are   spiked into a 1 L sample,  and  the  sample  is  ex- tracted by one of three procedures:

      - Samples containing no visible par- ticles are extracted with methylene chloride in a separatory funnel or by the solid-phase extraction technique summarized in Section

2.1.1.3. The extract is concentrated for clean- up.

      - Samples containing visible par- ticles are vacuum filtered through a glass- fiber filter. The filter is extracted in a Soxh- let/Dean-Stark (SDS) extractor (Reference 7), and the filtrate is extracted with meth- ylene chloride in a separatory funnel. The methylene chloride extract is concentrated and combined with the SDS extract prior to cleanup.

      - The sample is vacuum filtered through a glass-fiber filter on top of a solid- phase extraction (SPE) disk. The filter and disk are extracted in an SDS extractor, and the extract is concentrated for cleanup.

    - Solid, semi-solid, and multi-phase samples (but not tissue)—The labeled com- pounds are spiked into a sample containing

10 g (dry weight) of solids. Samples con- taining multiple phases are pressure filtered and any aqueous liquid is discarded. Coarse solids are ground or homogenized. Any non- aqueous liquid from multi-phase samples is combined with the solids and extracted in an SDS extractor. The extract is  concentrated for cleanup.

    - Fish and other tissue—The sample is extracted by one of two procedures:

      - Soxhlet or SDS extraction—A 20 g aliquot of sample is homogenized, and a 10 g aliquot is spiked  with  the  labeled  com- pounds. The sample is mixed with sodium sulfate, allowed to dry for 12–24 hours, and extracted for 18–24 hours using methylene chloride:hexane (1:1) in a Soxhlet extractor. The extract is evaporated to dryness, and the lipid  content  is  determined.

      - HCl digestion—A  20 g  aliquot is ho- mogenized, and a 10 g aliquot is placed in a bottle and  spiked  with the labeled com- pounds. After equilibration, 200 mL of hydro- chloric acid and 200 mL of methylene chlo- ride:hexane (1:1) are added, and the bottle is agitated for 12–24 hours. The extract is evap- orated to dryness, and the lipid content is determined.

  - After extraction, 37Cl4-labeled 2,3,7,8- TCDD is added to each extract  to  measure the efficiency of the cleanup process. Sample cleanups may include back-extraction with acid and/or base, and gel permeation, alu- mina, silica gel, Florisil and activated car- bon chromatography. High-performance liq- uid chromatography (HPLC) can be used for further isolation of the 2,3,7,8-isomers  or other specific isomers or congeners. Prior to the cleanup procedures cited above, tissue extracts are cleaned up using an anthropo- genic isolation column, a batch silica gel ad- sorption, or sulfuric acid and base back-ex- traction, depending on the tissue extraction procedure used.

  - After cleanup, the extract is con- centrated to near dryness. Immediately prior to injection, internal standards are added to each extract, and an aliquot of the extract is injected into the gas chromatograph. The analytes are separated by the GC and de- tected by a high-resolution (10,000) mass spectrometer. Two exact m/z’s are monitored for each analyte.

  - An individual CDD/CDF is identified by comparing the GC retention time and ion- abundance ratio of two exact m/z’s with the corresponding retention time of an authentic standard and the theoretical or acquired ion- abundance ratio of the two exact m/z’s. The non-2,3,7,8 substituted isomers and congeners are identified when retention times and ion- abundance ratios agree within predefined limits. Isomer specificity for 2,3,7,8-TCDD and 2,3,7,8-TCDF is achieved using GC col- umns that resolve these isomers from the other tetra-isomers.

  - Quantitative analysis is performed using selected ion current profile (SICP) areas, in one of three ways:

    - For the 15 2,3,7,8-substituted CDDs/ CDFs with labeled analogs (see Table 1), the GC/MS system is calibrated, and the con- centration of each compound is determined using the isotope dilution technique.

#### Pt. 136, App. A, Meth. 1613

    - For 1,2,3,7,8,9-HxCDD, OCDF, and the labeled compounds, the GC/MS system is calibrated and the concentration of each compound is determined using the internal standard technique.

    - For non-2,3,7,8-substituted isomers and for all isomers at a given level of chlorination (i.e., total TCDD), concentra- tions are determined using response factors from calibration of the CDDs/CDFs at the same level of chlorination.

2.6 The quality of the analysis is assured through reproducible  calibration  and  testing of the extraction, cleanup, and GC/MS sys- tems.

3.0   Definitions

Definitions are given in the glossary at the end of this method.

4.0   Contamination and Interferences

  - Solvents, reagents, glassware, and other sample processing hardware may yield artifacts and/or elevated baselines causing misinterpretation of chromatograms (Ref- erences 8–9). Specific selection of reagents and purification of solvents by distillation in all-glass systems may be required. Where possible, reagents are cleaned by extraction or solvent rinse.

  - Proper cleaning of glassware is ex- tremely important, because glassware may not only contaminate the samples but may also remove the analytes of interest by ad- sorption on the glass surface.

    - Glassware should be rinsed with sol- vent and washed with a detergent solution as soon after use as is practical. Sonication of glassware containing  a  detergent  solution for approximately 30 seconds may aid in cleaning. Glassware with removable parts, particularly separatory funnels with fluoropolymer stopcocks, must be disassem- bled prior to detergent washing.

    - After detergent washing, glassware should be rinsed immediately, first with methanol, then with hot tap water. The tap water rinse is followed by another methanol rinse, then acetone, and then methylene chloride.

    - Do not bake reusable glassware in an oven as a routine part of cleaning. Baking may be warranted after particularly dirty samples are encountered but should be mini- mized, as repeated baking of glassware may cause active sites on the glass surface that will irreversibly adsorb CDDs/CDFs.

    - Immediately prior to use, the  Soxh- let apparatus should be pre-extracted with toluene for approximately three hours (see Sections 12.3.1 through 12.3.3). Separatory funnels should be shaken with methylene chloride/toluene (80/20 mixture) for two min- utes, drained, and then shaken with pure methylene chloride for two minutes.

#### 40 CFR Ch. I (7–1–17 Edition)

  - All materials used in  the  analysis shall be demonstrated to be free from inter- ferences by running reference matrix method blanks initially and with each sample batch (samples started through the extraction process on a given 12-hour shift, to a max- imum of 20 samples).

    - The reference matrix must  simulate, as closely as possible, the sample  matrix under test. Ideally, the reference matrix should not contain the CDDs/CDFs in detect- able amounts, but should contain potential interferents in the concentrations  expected to be found in the samples to  be  analyzed. For example, a reference sample of human adipose	tissue	containing pentachloronaphthalene can be used to exer- cise the cleanup systems when samples con- taining pentachloronaphthalene are ex- pected.

    - When a reference matrix that simu- lates the sample matrix under test is not available, reagent water (Section 7.6.1)  can be used to simulate water samples; play- ground sand (Section 7.6.2) or white quartz sand (Section 7.3.2) can be used to simulate soils; filter paper (Section 7.6.3) can be used to simulate  papers  and  similar  materials; and corn oil (Section 7.6.4) can be used to simulate  tissues.

  - Interferences coextracted from sam- ples will vary considerably from source to source, depending on the diversity of the site being sampled. Interfering compounds may be present at concentrations  several  orders of magnitude higher than the CDDs/CDFs. The most frequently encountered inter- ferences are chlorinated biphenyls, methoxy biphenyls,	hydroxydiphenyl	ethers, benzylphenyl ethers, polynuclear aromatics, and pesticides. Because very low levels of CDDs/CDFs are measured by this method, the elimination of interferences is essential. The cleanup steps given in Section 13 can be used to reduce or eliminate these inter- ferences and thereby permit reliable deter- mination of the CDDs/CDFs at the levels shown in Table 2.

  - Each piece of reusable glassware should be numbered to associate that glass- ware with the processing of a particular sam- ple. This will assist the laboratory in track- ing possible sources of contamination for in- dividual samples, identifying glassware asso- ciated with highly contaminated samples that may require extra cleaning, and deter- mining when glassware should be discarded.

  - Cleanup of tissue—The natural lipid content of tissue can interfere in the anal- ysis of tissue samples for the CDDs/CDFs. The lipid  contents of different species and portions of tissue can vary widely. Lipids are soluble to varying degrees in various organic solvents and may be present in sufficient quantity to overwhelm the column chromatographic cleanup procedures used for cleanup of sample extracts. Lipids must

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1613

be removed by the lipid removal procedures in Section 13.7, followed by alumina (Section 13.4) or Florisil (Section 13.8), and carbon (Section 13.5)  as  minimum  additional  clean- up steps. If chlorodiphenyl ethers are de- tected, as indicated by the presence of peaks at the exact m/z’s monitored for these interferents, alumina and/or Florisil cleanup must be employed to eliminate these inter- ferences.

5.0   Safety

  - The toxicity or carcinogenicity of each compound or reagent used in this meth- od has not been precisely determined; how- ever, each chemical compound should be treated as a potential health hazard. Expo- sure to these compounds should be reduced to the lowest possible level.

    - The 2,3,7,8-TCDD isomer has been found to be acnegenic, carcinogenic, and teratogenic in laboratory  animal  studies.  It is soluble in water to approximately 200 ppt and in organic solvents to 0.14%. On the basis of the available toxicological and physical properties of 2,3,7,8-TCDD, all of the CDDs/ CDFs should be handled only by highly trained personnel thoroughly familiar with handling and cautionary procedures and the associated  risks.

    - It is recommended that the labora- tory purchase dilute standard solutions of the analytes in this method. However, if pri- mary solutions are prepared, they shall be prepared in a hood, and a NIOSH/MESA ap- proved toxic gas respirator shall be worn when high concentrations are handled.

  - The laboratory is responsible for maintaining  a  current  awareness  file  of OSHA regulations regarding the safe  han- dling of the chemicals specified in  this  meth- od. A reference file of material safety data sheets (MSDSs)  should  also  be  made  avail- able to all personnel involved in these anal- yses. It is also suggested that the laboratory perform personal hygiene monitoring of each analyst who uses this method and that the results of this monitoring  be  made  available to the analyst. Additional information on laboratory safety can be found in References 10–13. The references and bibliography at the end of Reference 13 are particularly com- prehensive in dealing with the general sub- ject  of  laboratory  safety.

  - The CDDs/CDFs and samples suspected to contain these compounds are handled using essentially the same techniques em- ployed in handling radioactive or infectious materials. Well-ventilated, controlled access laboratories are required. Assistance in eval- uating the health hazards of particular lab- oratory conditions may be obtained from certain consulting laboratories and from State Departments of Health or Labor, many of which have an industrial health service. The CDDs/CDFs are extremely toxic to lab- oratory  animals.  Each  laboratory  must  de-

velop a strict safety program for handling these compounds. The practices in Ref- erences 2 and 14 are highly recommended.

    - Facility—When finely divided sam- ples (dusts, soils, dry chemicals) are handled, all operations (including removal of samples from sample containers, weighing, transfer- ring, and mixing) should be performed in a glove box demonstrated to be leak tight or in a fume hood demonstrated to have adequate air flow. Gross losses to the laboratory ven- tilation system must not be allowed. Han- dling of the dilute solutions normally used in analytical and animal work presents no in- halation hazards except in the case of an ac- cident.

    - Protective equipment—Disposable plastic gloves, apron or lab coat, safety glasses or mask, and a glove box or fume hood adequate for radioactive work  should be used. During analytical operations that may give rise to aerosols or dusts, personnel should wear respirators equipped with acti- vated carbon filters. Eye protection equip- ment (preferably full face shields) must be worn while working with exposed samples or pure analytical standards. Latex gloves are commonly used to reduce exposure of the hands. When handling samples suspected or known to contain high concentrations of the CDDs/CDFs, an additional set of gloves can also be worn beneath the latex gloves.

    - Training—Workers must be trained in the proper method of removing contami- nated gloves and  clothing  without  con- tacting  the  exterior  surfaces.

    - Personal hygiene—Hands and fore- arms should be washed thoroughly after each manipulation and before breaks  (coffee, lunch, and shift).

    - Confinement—Isolated work areas posted with signs, segregated glassware and tools, and plastic absorbent paper on bench tops will aid in confining contamination.

    - Effluent vapors—The effluents of sample splitters from the gas chromatograph (GC) and from roughing pumps on the mass spectrometer (MS) should pass through ei- ther a column of activated charcoal or be bubbled through a trap containing oil or high-boiling alcohols to condense CDD/CDF vapors.

    - Waste Handling—Good technique in- cludes minimizing contaminated waste. Plastic bag liners should be used in waste cans. Janitors and other personnel must be trained in the safe handling of waste.

    - Decontamination

      - Decontamination of personnel—Use any mild soap with plenty of scrubbing ac- tion.

      - Glassware, tools, and surfaces— Chlorothene NU Solvent is the least toxic solvent shown to be effective. Satisfactory cleaning may be accomplished by rinsing with Chlorothene, then washing with any de- tergent and water. If glassware is first rinsed

#### Pt. 136, App. A, Meth. 1613

with solvent, then the dish water may be dis- posed of in the sewer. Given the cost of dis- posal, it is prudent to minimize solvent wastes.

    - Laundry—Clothing known to be con- taminated should be collected in  plastic bags. Persons who convey the bags and laun- der the clothing should be advised of the haz- ard and trained in proper handling. The clothing may be put into a washer without contact if the launderer knows of the poten- tial problem. The washer should be run through a cycle before being used again for other clothing.

    - Wipe tests—A useful method of de- termining cleanliness of work surfaces and tools is to wipe the surface with a piece of filter paper. Extraction and analysis by GC with an electron capture detector (ECD) can achieve a limit of detection of 0.1 g per wipe; analysis using this method can achieve an even lower detection limit. Less than 0.1

g per wipe indicates acceptable cleanliness; anything higher  warrants  further cleaning. More than 10 g on a wipe constitutes an acute hazard and requires prompt cleaning before further use of the equipment or work space, and indicates that unacceptable work practices have been employed.

    - Table or wrist-action shaker—The use of a table or wrist-action shaker for ex- traction of tissues presents the possibility of breakage of the extraction bottle and spill- age of acid and flammable organic solvent. A secondary containment system around the shaker is suggested to prevent the spread of acid and solvents in the event of such a breakage. The speed and intensity of shaking action should also be adjusted to minimize the possibility of breakage.

6.0   Apparatus and Materials

NOTE: Brand names, suppliers, and part numbers are for illustration purposes only and no endorsement is implied. Equivalent performance may be achieved using appa- ratus and materials other than those speci- fied here. Meeting the performance require- ments of this method is the responsibility of the laboratory.

  - Sampling Equipment for Discrete or Composite Sampling

    - Sample bottles and caps

      - Liquid samples (waters, sludges and similar materials containing 5% solids or less)—Sample bottle, amber glass, 1.1 L min- imum, with screw cap.

      - Solid samples (soils, sediments, sludges, paper  pulps,  filter  cake,  compost, and similar materials that  contain  more than 5% solids)—Sample bottle, wide mouth, amber glass, 500 mL minimum.

      - If amber bottles are not available, samples shall be protected from light.

#### 40 CFR Ch. I (7–1–17 Edition)

      - Bottle caps—Threaded to fit sample bottles. Caps shall be lined with fluoropolymer.

      - Cleaning

        - Bottles are detergent water washed, then solvent rinsed before use.

        - Liners  are  detergent  water washed, rinsed with reagent water (Section 7.6.1) followed by solvent, and baked at ap- proximately 200 C for a minimum of 1 hour prior to use.

6.1.2 Compositing  equipment—Automatic or manual compositing system incorporating glass containers cleaned per bottle cleaning procedure above. Only glass or fluoropolymer tubing shall be used. If the sampler uses a peristaltic pump, a minimum length of com- pressible silicone rubber tubing may be used in the pump only. Before use, the tubing shall be thoroughly rinsed with methanol, followed by repeated rinsing with reagent water to  minimize  sample  contamination. An integrating flow meter is used to collect proportional composite samples.

  - Equipment for Glassware Cleaning— Laboratory sink with overhead fume hood.

  - Equipment for Sample Preparation

    - Laboratory fume hood of sufficient size to contain the sample preparation equip- ment listed below.

    - Glove box (optional).

    - Tissue homogenizer—VirTis Model 45 Macro homogenizer (American Scientific Products H–3515, or equivalent) with stain- less  steel  Macro-shaft  and  Turbo-shear  blade.

    - Meat grinder—Hobart, or equivalent, with 3–5 mm holes in inner plate.

    - Equipment for determining percent moisture

      - Oven—Capable of maintaining a temperature of 110 5 C.

      - Dessicator.

    - Balances

      - Analytical—Capable of weighing 0.1 mg.

      - Top loading—Capable  of  weighing 10 mg.

  - Extraction Apparatus

    - Water samples

      - pH meter, with combination glass electrode.

      - pH paper, wide range (Hydrion Pa- pers, or equivalent).

      - Graduated cylinder, 1 L capacity.

      - Liquid/liquid	extraction—Sepa- ratory funnels, 250 mL, 500 mL, and 2000 mL, with   fluoropolymer   stopcocks.

      - Solid-phase extraction

        - One liter filtration apparatus, in- cluding glass funnel,  glass  frit  support, clamp, adapter, stopper, filtration flask, and vacuum tubing (Figure 4). For wastewater samples,  the  apparatus  should  accept  90  or

144 mm disks. For drinking water or other samples containing low solids, smaller disks may be used.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1613

        - Vacuum source capable of main- taining 25 in. Hg, equipped with shutoff valve and vacuum gauge.

        - Glass-fiber filter—Whatman GMF 150 (or equivalent), 1 micron pore size, to fit filtration apparatus in Section 6.4.1.5.1.

        - Solid-phase extraction disk con- taining octadecyl (C18) bonded silica uni- formly enmeshed  in  an  inert matrix—Fisher Scientific 14–378F (or equivalent), to fit fil- tration apparatus in Section 6.4.1.5.1.

    - Soxhlet/Dean-Stark (SDS) extractor (Figure 5)—For filters and solid/sludge sam- ples.

      - Soxhlet—50 mm ID, 200 mL capac- ity with 500 mL flask (Cal-Glass LG–6900, or equivalent, except substitute 500 mL round- bottom flask for 300 mL flat-bottom flask).

      - Thimble—43  123  to  fit  Soxhlet

(Cal-Glass LG–6901–122, or equivalent).

      - Moisture trap—Dean Stark or Bar- ret with fluoropolymer stopcock, to fit Soxh- let.

      - Heating  mantle—Hemispherical,   to fit 500 mL round-bottom flask (Cal-Glass LG– 8801–112, or equivalent).

      - Variable     transformer—Powerstat (or equivalent), 110 volt, 10 amp.

    - Apparatus for extraction of tissue.

      - Bottle for extraction (if digestion/ extraction using HCl is used)’’ 500–600 mL wide-mouth clear glass, with fluoropolymer- lined  cap.

      - Bottle for back-extraction—100–200 mL narrow-mouth clear glass with fluoropolymer-lined cap.

      - Mechanical    shaker—Wrist-action or platform-type rotary shaker that pro- duces	vigorous	agitation	(Sybron Thermolyne Model LE ‘‘Big Bill’’ rotator/ shaker, or equivalent).

      - Rack attached to shaker table to permit agitation of four to nine samples si- multaneously.

    - Beakers—400–500 mL.

    - Spatulas—Stainless steel.

  - Filtration Apparatus.

    - Pyrex glass wool—Solvent-extracted by SDS for three hours minimum.

NOTE: Baking glass wool may cause active sites that will irreversibly adsorb CDDs/ CDFs.

    - Glass funnel—125–250 mL.

    - Glass-fiber filter paper—Whatman GF/D (or equivalent), to fit glass funnel in Section 6.5.2.

    - Drying column—15–20 mm ID Pyrex chromatographic column equipped with coarse-glass frit or glass-wool plug.

    - Buchner funnel—15 cm.

    - Glass-fiber filter paper—to fit Buchner funnel in Section 6.5.5.

    - Filtration flasks—1.5–2.0 L, with side arm.

    - Pressure filtration apparatus— Millipore YT30 142 HW, or equivalent.

  - Centrifuge Apparatus.

    - Centrifuge—Capable of rotating 500 mL centrifuge bottles or 15 mL centrifuge tubes at 5,000 rpm minimum.

    - Centrifuge bottles—500 mL, with screw-caps, to fit centrifuge.

    - Centrifuge tubes—12–15 mL, with screw-caps, to fit centrifuge.

  - Cleanup Apparatus.

    - Automated gel permeation chro- matograph  (Analytical  Biochemical  Labs, Inc, Columbia, MO, Model GPC Autoprep 1002, or equivalent).

      - Column—600–700  mm  long  25  mm

ID, packed with 70 g of

SX–3 Bio-beads (Bio-Rad Laboratories, Rich- mond, CA, or equivalent).

      - Syringe—10 mL, with Luer fitting.

      - Syringe filter  holder—stainless steel, and glass-fiber or fluoropolymer filters (Gelman 4310, or equivalent).

      - UV detectors—254 nm, preparative or  semi-preparative  flow  cell  (Isco,   Inc., Type 6; Schmadzu, 5 mm path length; Beck- man-Altex 152W, 8 L micro-prep flow cell, 2 mm path; Pharmacia UV–1, 3 mm flow cell; LDC Milton-Roy UV–3, monitor #1203; or equivalent).

    - Reverse-phase high-performance liq- uid  chromatograph.

      - Column oven and detector—Perkin- Elmer Model LC–65T (or equivalent) operated at 0.02 AUFS at 235 nm.

      - Injector—Rheodyne 7120 (or equiva- lent) with 50 L sample loop.

      - Column—Two   6.2   mm   250   mm

Zorbax-ODS columns in series (DuPont In- struments Division, Wilmington, DE, or equivalent), operated at 50 C with 2.0 mL/ min  methanol  isocratic  effluent.

      - Pump—Altex 110A (or  equivalent).

    - Pipets.

      - Disposable, pasteur—150 mm long  5-mm ID (Fisher Scientific 13–678–6A, or equivalent).

      - Disposable, serological—10 mL (6 mm ID).

    - Glass chromatographic columns.

      - 150 mm long 8-mm ID, (Kontes K– 420155, or equivalent) with  coarse-glass  frit or glass-wool plug and 250 mL reservoir.

      - 200   mm   long   15   mm   ID,   with

coarse-glass frit or glass-wool plug and  250 mL  reservoir.

      - 300  mm  long  25  mm  ID,  with  300

mL reservoir and glass or fluoropolymer stopcock.

    - Stirring apparatus for batch silica cleanup of tissue extracts.

      - Mechanical stirrer—Corning Model 320, or equivalent.

      - Bottle—500–600 mL wide-mouth clear  glass.

6.7.6 Oven—For baking and storage of ad- sorbents, capable of maintaining a constant temperature (5 C) in the range of 105–250 C.

  - Concentration Apparatus.

#### Pt. 136, App. A, Meth. 1613

    - Rotary	evaporator—Buchi/ Brinkman-American Scientific No. E5045–10 or equivalent, equipped with a variable tem- perature water bath.

      - Vacuum source for  rotary evapo- rator equipped with shutoff valve at the evaporator and vacuum gauge.

      - A recirculating water pump and chiller are recommended, as use of tap water for cooling the evaporator wastes large vol- umes of water and can lead to inconsistent performance as water temperatures and pres- sures vary.

      - Round-bottom  flask—100  mL  and

500  mL  or  larger,  with  ground-glass  fitting compatible with the rotary evaporator.

    - Kuderna-Danish  (K-D)  Concentrator.

      - Concentrator tube—10 mL, grad- uated (Kontes K–570050–1025, or equivalent) with calibration verified. Ground-glass stop- per (size 19/22 joint) is used to prevent evapo- ration  of  extracts.

      - Evaporation flask—500 mL (Kontes K–570001–0500, or equivalent), attached to concentrator tube with springs (Kontes K– 662750–0012 or equivalent).

      - Snyder column—Three-ball macro (Kontes K–503000–0232, or equivalent).

      - Boiling chips.

        - Glass or silicon carbide—Approxi- mately 10/40 mesh, extracted with methylene chloride and baked at 450 C for one hour minimum.

        - Fluoropolymer (optional)—Ex- tracted with methylene chloride.

      - Water bath—Heated, with concen- tric ring cover, capable of maintaining a temperature within 2 C, installed in a fume hood.

    - Nitrogen blowdown apparatus— Equipped with water bath controlled in the range of 30–60 C (N-Evap, Organomation As- sociates, Inc., South Berlin, MA, or equiva- lent), installed in a fume hood.

    - Sample vials.

      - Amber glass—2–5 mL with fluoropolymer-lined screw-cap.

      - Glass—0.3 mL, conical, with fluoropolymer-lined screw or crimp cap.

  - Gas Chromatograph—Shall have splitless or on-column injection port for cap- illary column, temperature program with isothermal hold, and shall meet all of the performance specifications in Section 10.

    - GC column for CDDs/CDFs and for isomer specificity for 2,3,7,8-TCDD—60 5 m long 0.32 0.02 mm ID; 0.25 m 5% phenyl, 94% methyl, 1% vinyl silicone bonded-phase fused-silica capillary column (J&W DB–5, or equivalent).

    - GC column for isomer specificity for 2,3,7,8-TCDF—30 5 m long 0.32 0.02 mm ID;

0.25  m  bonded-phase  fused-silica  capillary column (J&W DB–225, or equivalent).

  - Mass Spectrometer—28–40 eV electron impact ionization, shall be capable of repet- itively selectively monitoring 12 exact m/z’s

#### 40 CFR Ch. I (7–1–17 Edition)

minimum at high resolution (10,000) during a period of approximately one second, and shall meet all of the performance specifica- tions in Section 10.

  - GC/MS Interface—The mass spec- trometer (MS) shall be interfaced to the GC such that the end of the capillary column terminates within 1 cm of the ion source but does not intercept the electron or ion beams.

  - Data System—Capable of collecting, recording, and storing MS data.

7.0   Reagents and Standards

  - pH Adjustment and Back-Extraction.

    - Potassium hydroxide—Dissolve 20 g reagent grade KOH in 100 mL reagent water.

    - Sulfuric acid—Reagent grade (spe- cific gravity 1.84).

    - Hydrochloric acid—Reagent grade, 6N.

    - Sodium chloride—Reagent grade, prepare at 5% (w/v) solution in  reagent water.

  - Solution Drying and Evaporation.

    - Solution drying—Sodium sulfate, re- agent grade,  granular,   anhydrous   (Baker 3375, or equivalent), rinsed with methylene chloride (20 mL/g), baked at 400 C for one hour minimum, cooled in a dessicator,  and stored in a pre-cleaned glass bottle with screw-cap that prevents moisture from en- tering. If, after heating, the sodium sulfate develops  a  noticeable  grayish  cast  (due   to the presence of  carbon  in  the  crystal  ma- trix),  that  batch  of  reagent  is   not   suitable for use and should be discarded. Extraction with methylene chloride (as opposed to  sim- ple rinsing) and baking at a lower tempera- ture may produce sodium sulfate that is suitable  for  use.

    - Tissue drying—Sodium sulfate, rea- gent grade, powdered, treated and stored as above.

    - Prepurified nitrogen.

  - Extraction.

    - Solvents—Acetone,	toluene, cyclohexane, hexane, methanol, methylene chloride, and nonane; distilled in glass, pes- ticide quality, lot-certified to be free of interferences.

    - White quartz sand, 60/70 mesh—For Soxhlet/Dean-Stark extraction (Aldrich Chemical, Cat. No. 27–437–9, or equivalent). Bake at 450 C for four hours minimum.

  - GPC Calibration Solution—Prepare a solution containing 300 mg/mL corn oil, 15 mg/mL bis(2-ethylhexyl)  phthalate,  1.4  mg/ mL pentachlorophenol, 0.1 mg/mL perylene, and 0.5 mg/mL sulfur.

  - Adsorbents for Sample Cleanup.

    - Silica gel.

      - Activated silica gel—100–200 mesh, Supelco 1–3651 (or equivalent), rinsed with methylene chloride, baked at 180 C for a minimum of one hour, cooled in a  dessicator, and  stored  in  a  precleaned  glass  bottle  with

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1613

screw-cap that prevents moisture from en- tering.

      - Acid silica gel (30% w/w)—Thor- oughly mix 44.0 g of concentrated sulfuric acid with 100.0 g of activated silica gel in a clean container. Break up aggregates with a stirring rod until a uniform mixture is ob- tained. Store in a bottle with a fluoropolymer-lined screw-cap.

      - Basic silica gel—Thoroughly mix 30 g of 1N sodium hydroxide with 100 g of acti- vated silica gel in a  clean  container.  Break up aggregates with a stirring rod until a uni- form mixture is obtained. Store in a bottle with a fluoropolymer-lined screw-cap.

      - Potassium silicate.

        - Dissolve 56 g of high purity potas- sium hydroxide (Aldrich, or equivalent) in 300 mL of methanol in a 750–1000 mL flat-bot- tom  flask.

        - Add 100  g of silica gel and a stir- ring bar, and stir on a hot plate at 60–70 C for one to two hours.

        - Decant the liquid and rinse the potassium silicate twice with 100 mL por- tions of methanol, followed by a single rinse with 100 mL of methylene chloride.

        - Spread the potassium silicate on solvent-rinsed aluminum foil and dry for two to four hours in a hood.

        - Activate overnight at 200–250 C.

    - Alumina—Either one of two types of alumina, acid or basic, may be used in the cleanup of sample extracts, provided that the laboratory can meet the performance speci- fications for the recovery of labeled com- pounds described in Section 9.3. The same type of alumina must be used for all samples, including those used to demonstrate initial precision and recovery (Section 9.2) and on- going precision and recovery (Section 15.5).

      - Acid alumina—Supelco 19996–6C (or equivalent). Activate  by  heating  to  130  C  for a minimum of 12 hours.

      - Basic alumina—Supelco 19944–6C (or equivalent). Activate by heating to 600 C for a minimum of 24 hours. Alternatively, ac- tivate by heating in a tube furnace at 650–700

C under an air flow rate of approximately 400 cc/minute. Do not heat over 700 C, as this can lead to reduced capacity for  retaining the analytes. Store at 130 C in a covered flask. Use within five days of baking.

    - Carbon.

      - Carbopak C—(Supelco 1–0258, or equivalent).

      - Celite 545—(Supelco 2–0199, or equivalent).

      - Thoroughly mix  9.0  g  Carbopak  C and 41.0 g Celite 545 to produce an 18% w/w mixture. Activate the mixture at 130 C for a minimum  of  six  hours.  Store  in  a  dessicator.

    - Anthropogenic isolation column— Pack the column in Section 6.7.4.3 from bot- tom to top with the following:

      - 2 g silica gel (Section  7.5.1.1).

      - 2 g potassium silicate  (Section 7.5.1.4).

      - 2 g granular anhydrous sodium sul- fate (Section 7.2.1).

      - 10 g acid silica gel (Section 7.5.1.2).

      - 2 g granular anhydrous sodium sul- fate.

    - Florisil column.

      - Florisil—60–100 mesh, Floridin Corp (or equivalent). Soxhlet extract in 500 g por- tions for 24 hours.

      - Insert a glass wool plug into the ta- pered end of a graduated serological pipet (Section 6.7.3.2). Pack with 1.5 g (approx 2 mL) of Florisil topped with approx 1 mL of sodium sulfate (Section 7.2.1) and a glass wool plug.

      - Activate in an oven at 130–150 C for

a minimum of 24 hours and cool for 30 min- utes. Use within 90 minutes of cooling.

  - Reference  Matrices—Matrices   in which the CDDs/CDFs and interfering com- pounds are not detected by this method.

    - Reagent water—Bottled water pur- chased locally, or prepared by passage through  activated  carbon.

    - High-solids reference matrix—Play- ground sand or similar material. Prepared by extraction with methylene chloride and/or baking at 450 C for a minimum of four hours.

    - Paper reference matrix—Glass-fiber filter, Gelman Type A, or  equivalent.  Cut paper to simulate the surface area of the paper sample being tested.

    - Tissue reference matrix—Corn or other vegetable oil. May be prepared by ex- traction  with  methylene  chloride.

    - Other matrices—This method may be verified on any reference matrix by per- forming the tests given in Section 9.2. Ideal- ly, the matrix should be free of the CDDs/ CDFs, but in no case shall the background level of the CDDs/CDFs in the reference ma- trix exceed three times  the  minimum  levels in Table 2. If low background levels of the CDDs/CDFs are present in the reference ma- trix, the spike level of the analytes used in Section 9.2 should be increased to provide a spike-to-background ratio in the range of 1:1 to 5:1 (Reference 15).

  - Standard Solutions—Purchased as so- lutions or mixtures with  certification  to their purity, concentration,  and  authen- ticity, or prepared from materials of known purity and composition. If the chemical pu- rity is 98% or greater, the weight may be used without correction to compute the con- centration of the standard. When not being used, standards are stored in the dark at room temperature in screw-capped vials with fluoropolymer-lined caps. A mark is  placed on the vial at the level of the  solution  so that solvent loss by evaporation can be de- tected. If solvent loss has occurred, the solu- tion should be replaced.

  - Stock Solutions.

#### Pt. 136, App. A, Meth. 1613

    - Preparation—Prepare in nonane per the steps below or purchase as dilute solu- tions (Cambridge Isotope Laboratories (CIL), Woburn, MA, or equivalent). Observe the safety precautions in Section 5, and the rec- ommendation in Section 5.1.2.

    - Dissolve an appropriate amount of assayed reference material in solvent. For example, weigh 1–2 mg of 2,3,7,8-TCDD to three significant figures in a 10 mL ground- glass-stoppered volumetric flask and fill to the mark with nonane. After the TCDD is completely dissolved,  transfer  the  solution to a clean 15 mL vial with fluoropolymer- lined cap.

    - Stock standard solutions should be checked for signs of degradation prior to the preparation of calibration  or  performance test standards. Reference standards that can be used to determine the accuracy of calibra- tion standards are available from CIL and may be available from other vendors.

  - PAR Stock Solution

    - All CDDs/CDFs—Using the solutions in Section 7.8, prepare the PAR stock solu- tion to contain the CDDs/CDFs at the con- centrations shown in Table 3. When diluted, the solution will become the PAR (Section 7.14).

    - If only 2,3,7,8-TCDD and 2,3,7,8-TCDF are to be determined, prepare the PAR stock solution to contain these compounds only.

  - Labeled-Compound Spiking Solution.

    - All CDDs/CDFs—From stock solu- tions, or from purchased mixtures, prepare this solution to contain the labeled com- pounds in nonane at the concentrations shown in Table 3. This solution is diluted with acetone prior to use (Section 7.10.3).

7.10.2 If only 2,3,7,8-TCDD and 2,3,7,8- TCDF are to be determined, prepare the la- beled-compound solution to contain these compounds only. This solution  is  diluted with acetone prior to use (Section 7.10.3).

7.10.3 Dilute  a sufficient volume of  the la- beled compound  solution (Section  7.10.1 or 7.10.2) by a factor of 50 with acetone to pre- pare a diluted spiking solution. Each sample requires 1.0 mL of the  diluted  solution,  but no  more  solution  should  be  prepared  than can be used in one day.

  - Cleanup Standard—Prepare 37Cl4- 2,3,7,8-TCDD in nonane at the concentration shown in Table 3. The cleanup standard is added to all extracts prior to cleanup to measure the efficiency of the cleanup proc- ess.

  - Internal Standard(s).

7.12.1 All CDDs/CDFs—Prepare the inter- nal standard solution to contain 13C12-1,2,3,4- TCDD and 13C2-1,2,3,7,8,9-HxCDD in nonane at the concentration shown in Table 3.

7.12.2 If only 2,3,7,8-TCDD and 2,3,7,8- TCDF are to be determined, prepare the in- ternal standard solution to contain 13C12- 1,2,3,4-TCDD only.

#### 40 CFR Ch. I (7–1–17 Edition)

  - Calibration Standards (CS1 through CS5)—Combine the solutions in Sections 7.9 through 7.12 to produce the five calibration solutions shown in Table 4 in nonane. These solutions permit the relative response  (la- beled to  native)  and response  factor  to  be measured as a function of concentration. The CS3 standard  is  used  for  calibration verification (VER). If only 2,3,7,8-TCDD and 2,3,7,8-TCDF are to be determined, combine the solutions appropriate to these  com- pounds.

  - Precision and Recovery (PAR) Stand- ard—Used for determination  of  initial  (Sec- tion 9.2) and ongoing (Section 15.5) precision and recovery. Dilute 10 L of the  precision and recovery standard (Section 7.9.1 or 7.9.2) to 2.0 mL with acetone for each  sample  ma- trix for each sample batch. One mL each are required for the blank and OPR  with  each matrix  in  each  batch.

  - GC Retention Time Window Defining Solution and Isomer Specificity Test Stand- ard—Used to define the beginning and ending retention times for the dioxin and furan iso- mers and to demonstrate  isomer  specificity of the GC columns employed for determina- tion of 2,3,7,8-TCDD and 2,3,7,8-TCDF. The standard must contain the compounds listed in Table 5 (CIL EDF—4006, or equivalent), at a minimum. It is not necessary  to  monitor the window-defining compounds if only 2,3,7,8-TCDD and 2,3,7,8-TCDF are to be de- termined. In this case, an isomer-specificity test standard containing the most closely eluted isomers listed in Table 5 (CIL EDF- 4033, or equivalent) may be used.

  - QC Check Sample—A QC Check Sam- ple should be obtained from a source inde- pendent of the calibration standards. Ideally, this check sample would be a certified ref- erence material containing the  CDDs/CDFs in known concentrations in a sample matrix similar to the matrix under test.

  - Stability of Solutions—Standard so- lutions used for quantitative purposes (Sec- tions 7.9 through 7.15) should be analyzed pe- riodically, and should be assayed against ref- erence standards (Section 7.8.3) before fur- ther use.

8.0  Sample Collection, Preservation, Storage, and Holding Times

  - Collect samples in amber glass con- tainers following conventional sampling practices (Reference 16). Aqueous samples that flow freely are collected in refrigerated bottles using automatic sampling equip- ment. Solid samples are collected as grab samples using wide-mouth jars.

  - Maintain aqueous samples in the dark at 0–4 C from the time of collection until re- ceipt at the  laboratory.  If  residual  chlorine is present in aqueous samples, add 80 mg so- dium   thiosulfate   per   liter   of   water.   EPA

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1613

Methods 330.4 and 330.5 may be used to meas- ure residual chlorine (Reference 17). If  sam- ple pH is greater than 9, adjust to pH  7–9 with  sulfuric  acid.

Maintain solid, semi-solid, oily, and mixed- phase samples in the dark at <4 C from the time of collection until receipt at the labora- tory.

Store  aqueous  samples  in  the  dark  at  0–4

C. Store solid, semi-solid, oily, mixed-phase, and tissue samples in the dark at <¥10 C.

  - Fish and Tissue Samples.

    - Fish may be cleaned, filleted, or processed in other ways in the field, such that the laboratory may expect to receive whole fish, fish fillets, or other tissues for analysis.

    - Fish collected in the field should be wrapped in aluminum foil, and must be maintained at a temperature less than 4 C from the time of collection until  receipt  at the  laboratory.

    - Samples must be frozen upon receipt at the laboratory and maintained in the dark at <¥10 C until prepared. Maintain unused sample in the dark at <¥10 C.

  - Holding Times.

    - There are no demonstrated max- imum holding times associated with CDDs/ CDFs in aqueous, solid,  semi-solid,  tissues, or other sample matrices. If stored in the dark at 0–4 C and preserved as given above (if required), aqueous samples may be stored for up to one year. Similarly, if stored in the dark at <¥10 C, solid, semi-solid,  multi- phase, and tissue samples may be stored for up to one year.

    - Store sample extracts in the dark at

<¥10 C until analyzed. If stored in the dark at <¥10 C, sample extracts may be stored for up to one year.

9.0   Quality Assurance/Quality Control

  - Each laboratory that uses this method is required to operate a formal quality assur- ance program (Reference 18). The minimum requirements of this program consist of an initial demonstration  of  laboratory  capa- bility, analysis of samples spiked with la- beled compounds to evaluate and document data quality, and analysis of standards and blanks as tests of continued performance. Laboratory performance is compared to es- tablished performance criteria to determine if the results of analyses meet the perform- ance characteristics of the method.

If the method is to be applied to sample matrix other than water (e.g., soils, filter cake, compost, tissue) the most appropriate alternate matrix (Sections 7.6.2 through 7.6.5) is substituted for the reagent water matrix (Section 7.6.1) in all performance tests.

    - The analyst shall make an initial demonstration of the ability to generate ac- ceptable  accuracy  and  precision  with  this

method.   This   ability   is   established   as   de- scribed in Section 9.2.

    - In recognition of advances that are occurring in analytical technology, and to allow the analyst to overcome sample ma- trix interferences, the analyst is permitted certain options to improve separations or lower the costs of measurements. These op- tions include alternate extraction, con- centration, cleanup procedures, and changes in columns and detectors. Alternate deter- minative techniques, such as the substi- tution of  spectroscopic or immuno-assay techniques, and changes that degrade meth- od performance, are not allowed. If an ana- lytical technique other than the techniques specified in this method is used, that tech- nique must have a specificity equal to or bet- ter than the specificity of the techniques in this method for the analytes of interest.

      - Each  time  a  modification   is   made to this method, the analyst is required to  re- peat the procedure in Section 9.2. If the de- tection limit of the method  will  be  affected by the change, the laboratory is required to demonstrate that the MDL (40 CFR part 136, appendix B) is lower than one-third the regu- latory compliance level  or  one-third  the  ML in this method, whichever is higher. If cali- bration will be affected by the change, the analyst must recalibrate the instrument per Section  10.

      - The laboratory is required to main- tain records of modifications made to this method. These records include the following, at a minimum:

        - The names, titles, addresses, and telephone numbers of the analyst(s) who per- formed the analyses and modification, and of the quality control officer who witnessed and will verify the analyses and modifications.

        - A listing of pollutant(s) meas- ured, by name and CAS Registry number.

        - A narrative stating reason(s) for the modifications.

        - Results from all quality control (QC) tests comparing the modified method to this method, including:

- Calibration (Section 10.5 through 10.7).

- Calibration verification (Section 15.3).

- Initial precision and recovery (Section 9.2).

- Labeled compound recovery (Section 9.3).

- Analysis of blanks (Section 9.5).

- Accuracy assessment (Section 9.4).

        - Data that will allow an inde- pendent reviewer to validate each deter- mination by  tracing  the  instrument output (peak height, area, or other signal) to the final result. These data are to include:

- Sample numbers and other identifiers.

- Extraction dates.

- Analysis dates and times.

- Analysis sequence/run chronology.

- Sample weight or volume (Section 11).

#### Pt. 136, App. A, Meth. 1613

- Extract volume prior to each cleanup step (Section 13).

- Extract volume after each cleanup step (Section 13).

- Final extract volume prior to injection (Section 14).

- Injection volume (Section 14.3).

- Dilution data, differentiating between dilution of a sample or extract (Section 17.5).

- Instrument and operating conditions.

- Column (dimensions, liquid phase, solid support,  film  thickness,  etc).

- Operating conditions (temperatures, temperature program, flow rates).

- Detector (type, operating conditions, etc).

- Chromatograms, printer tapes, and other recordings of raw data.

- Quantitation reports, data system out- puts, and other data to link the raw data to the results reported.

    - Analyses of method blanks are re- quired to demonstrate freedom from con- tamination (Section 4.3). The procedures and criteria for analysis of a method blank are described in Sections 9.5 and 15.6.

    - The laboratory shall spike all sam- ples with labeled compounds to monitor method performance. This test  is  described in Section 9.3. When results of these spikes indicate atypical method performance for samples, the samples are diluted to bring method performance within acceptable lim- its. Procedures for dilution are given in Sec- tion 17.5.

    - The laboratory shall, on an ongoing basis, demonstrate through calibration verification and the analysis of the ongoing precision and recovery aliquot that the ana- lytical system is in control.  These  proce- dures are described in Sections 15.1 through 15.5.

    - The laboratory shall  maintain records to define the quality of data that is generated. Development of accuracy state- ments is described in Section 9.4.

  - Initial Precision and Recovery (IPR)— To establish the ability to generate accept- able precision and recovery,  the  analyst shall perform the following operations.

    - For low solids (aqueous) samples, ex- tract, concentrate, and analyze four 1 L aliquots of reagent water spiked with the di- luted labeled compound spiking solution (Section 7.10.3) and the precision and recov- ery standard (Section 7.14) according to the procedures in Sections 11 through 18. For an alternative sample matrix, four aliquots of the alternative reference matrix (Section 7.6) are used. All sample processing steps  that are to be used for processing samples, includ- ing preparation (Section 11), extraction (Sec- tion 12), and cleanup (Section 13), shall be in- cluded in this test.

    - Using results of the set of four anal- yses, compute the average concentration (X) of the extracts in ng/mL and the standard de-

#### 40 CFR Ch. I (7–1–17 Edition)

viation of the concentration (s) in ng/mL for each compound, by isotope dilution for CDDs/CDFs with a labeled analog, and by in- ternal standard for 1,2,3,7,8,9-HxCDD, OCDF, and the labeled compounds.

    - For each CDD/CDF and labeled com- pound, compare s and X with the cor- responding limits for initial precision and re- covery in Table 6. If only 2,3,7,8-TCDD and 2,3,7,8-TCDF are to be determined, compare s and X with the corresponding limits for ini- tial precision and recovery in Table 6a.  If  s and X for all compounds meet the acceptance criteria, system performance  is  acceptable and analysis of blanks and samples  may begin. If, however, any individual s  exceeds the precision limit or any individual X falls outside the range for accuracy, system per- formance is unacceptable for that compound. Correct the problem and repeat the test (Sec- tion 9.2).

  - The laboratory shall spike all samples with the diluted labeled compound spiking solution (Section 7.10.3) to assess method performance on the sample matrix.

    - Analyze  each   sample   according   to the procedures in Sections 11 through 18.

    - Compute the percent recovery of the labeled compounds and the cleanup standard using the internal standard  method (Section 17.2).

    - The recovery of each labeled com- pound must be within the limits in Table 7 when all 2,3,7,8-substituted CDDs/CDFs are determined,  and  within  the  limits   in   Table 7a when only 2,3,7,8-TCDD and 2,3,7,8-TCDF are determined. If the recovery of any com- pound falls outside of these limits, method performance is unacceptable for that com- pound in that sample. To overcome such dif- ficulties, water samples are diluted  and smaller amounts of soils, sludges, sediments, and other matrices are reanalyzed per Sec- tion 18.4.

  - Recovery of labeled compounds from samples should be assessed and records should be maintained.

    - After the  analysis  of  five  samples  of a given matrix type  (water,  soil,  sludge, pulp, etc.)  for  which the  labeled  compounds pass the tests in Section 9.3, compute the av- erage percent recovery (R) and the standard deviation of the percent recovery (SR)  for the labeled compounds only. Express the as- sessment as a percent recovery interval from R¥2SR to R = 2SR for each matrix. For exam- ple, if R = 90% and SR = 10% for five analyses of pulp, the recovery interval is expressed as 70–110%.

    - Update the accuracy assessment for each labeled  compound in  each matrix  on  a regular basis (e.g., after each 5–10 new meas- urements).

  - Method Blanks—Reference matrix method blanks are analyzed to demonstrate freedom from contamination (Section 4.3).

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1613

    - Prepare, extract,  clean  up,  and con- centrate a method blank with  each  sample batch (samples of the same matrix started through the extraction process on the same 12-hour shift, to a maximum of 20  samples). The matrix for the method blank shall  be similar to  sample  matrix  for  the  batch,  e.g., a 1 L reagent water blank (Section 7.6.1), high-solids reference matrix blank (Section 7.6.2), paper matrix blank (Section 7.6.3); tis- sue blank (Section 7.6.4) or alternative ref- erence matrix blank (Section 7.6.5). Analyze the blank immediately after analysis of the OPR (Section 15.5) to demonstrate freedom from    contamination.

    - If any 2,3,7,8-substituted CDD/CDF (Table 1) is found in the blank at greater than the minimum level (Table 2) or one- third the regulatory compliance level, whichever is greater; or if any potentially interfering compound is found  in  the  blank at the minimum level for each level of chlorination given in Table 2 (assuming a re- sponse factor of 1 relative to the 13C12-1,2,3,4- TCDD internal standard for compounds not listed in Table 1), analysis of samples is halt- ed until the blank associated with  the  sam- ple batch shows no evidence of contamina- tion at this level.  All samples must  be asso- ciated with an  uncontaminated  method blank before the results for those samples may be reported for regulatory compliance purposes.

  - QC Check Sample—Analyze the QC Check Sample (Section 7.16) periodically to assure the accuracy of calibration standards and the overall reliability of the analytical process. It is suggested that the QC Check Sample be analyzed at least quarterly.

  - The specifications contained in this method can be met if the apparatus used is calibrated properly and then maintained in a calibrated state. The standards used for cali- bration (Section 10), calibration verification (Section 15.3), and for initial (Section 9.2) and ongoing (Section 15.5) precision and re- covery should be identical, so that the most precise results will be obtained. A GC/MS in- strument will provide the most reproducible results if dedicated to the settings and condi- tions required for the analyses of CDDs/CDFs by this method.

  - Depending on specific program re- quirements, field replicates may be collected to determine the precision of the sampling technique, and spiked samples may be re- quired to determine the accuracy of the analysis when the internal standard method is used.

10.0   Calibration

10.1 Establish the operating conditions necessary to meet the minimum retention times for the internal standards in Section

10.2.4 and the relative retention times for the CDDs/CDFs in Table 2.

    - Suggested GC operating  conditions:

Injector temperature: 270 C Interface temperature: 290  C Initial  temperature:  200  C Initial  time:  Two  minutes Temperature   program: 200–220 C, at 5 C/minute

220 C for 16 minutes

220–235 C, at 5 C/minute 235 C for seven minutes 235–330 C, at 5 C/minute

NOTE: All portions of the column that con- nect the GC to the ion source shall remain at or above the interface temperature specified above during analysis to preclude condensa- tion of less volatile compounds.

Optimize GC conditions for compound sep- aration and sensitivity. Once optimized, the same GC conditions must be used for the analysis of all standards, blanks, IPR and OPR aliquots, and samples.

    - Mass spectrometer (MS) resolu- tion—Obtain a selected ion current profile (SICP) of each analyte in Table 3 at the two exact m/z’s specified in Table 8 and at 10,000 resolving power by injecting an authentic standard of the CDDs/CDFs  either  singly  or as part of a mixture in which there is no in- terference between closely eluted  compo- nents.

      - The analysis time for CDDs/CDFs may exceed the long-term mass stability  of the mass spectrometer. Because the instru- ment is operated in the high-resolution mode, mass drifts of a few ppm (e.g., 5 ppm in mass) can have serious adverse effects on instrument performance. Therefore, a mass- drift correction is mandatory  and  a  lock- mass m/z from PFK is used for drift correc- tion. The lock-mass m/z is dependent on the exact m/z’s monitored within each descriptor, as shown in Table 8. The level of PFK metered into the HRMS during analyses should be  adjusted so  that  the amplitude  of the most intense selected lock-mass m/z sig- nal (regardless of the  descriptor  number) does not exceed 10% of the full-scale deflec- tion for a given set of detector parameters. Under those conditions, sensitivity changes that might occur during the analysis can be more effectively monitored.

NOTE: Excessive PFK (or any other ref- erence substance) may cause noise problems and contamination of the ion source necessi- tating increased frequency of source clean- ing.

      - If the HRMS has the capability to monitor resolution during the analysis, it is acceptable  to  terminate  the  analysis  when the resolution falls below 10,000 to save rea- nalysis   time.

      - Using a PFK molecular leak, tune the instrument to meet the minimum re- quired resolving power of 10,000 (10% valley) at m/z 304.9824 (PFK) or any other reference signal close to m/z 304 (from TCDF). For each

#### Pt. 136, App. A, Meth. 1613

descriptor (Table 8), monitor and record the resolution and exact m/z’s of three to five reference peaks covering the mass range  of the descriptor. The resolution must be great- er than or equal to 10,000, and the deviation between the exact m/z and the theoretical m/ z (Table 8) for each exact m/z monitored must be less than 5 ppm.

  - Ion Abundance Ratios, Minimum Lev- els, Signal-to-Noise Ratios, and Absolute Re- tention  Times—Choose  an  injection   volume of either 1 L or 2 L, consistent with the ca- pability of  the  HRGC/HRMS  instrument.  In- ject a 1 L or 2 L aliquot of the CS1 calibra- tion solution (Table 4) using the GC condi- tions from Section 10.1.1. If only 2,3,7,8-TCDD and 2,3,7,8-TCDF are to be determined, the operating   conditions   and    specifications below apply to analysis of those compounds only.

    - Measure the SICP areas for each analyte, and compute the ion abundance ra- tios at the exact m/z’s specified in Table 8. Compare the computed ratio to the theo- retical ratio given in Table 9.

      - The exact m/z’s to be monitored in each descriptor are shown in Table 8. Each group or descriptor shall be monitored in succession as a  function  of  GC  retention time to ensure that all CDDs/CDFs are de- tected. Additional m/z’s may be monitored in each descriptor, and the m/z’s may be divided among more  than  the  five  descriptors  listed in Table 8, provided that the laboratory is able to monitor the m/z’s of all the CDDs/ CDFs that may elute from the GC in a given retention-time window. If only 2,3,7,8-TCDD and 2,3,7,8-TCDF are to be determined, the descriptors may be modified to include only the exact m/z’s for the tetra-and penta-iso- mers, the diphenyl ethers, and the  lock  m/ z’s.

      - The mass spectrometer shall be operated in a mass-drift correction mode, using perfluorokerosene (PFK) to  provide lock m/z’s.  The lock-mass  for each  group of m/z’s is shown in Table 8. Each lock mass shall be monitored and shall not vary by more than 20% throughout its respective re- tention time window. Variations of the lock mass by more than 20% indicate the presence of coeluting interferences that may signifi- cantly reduce the sensitivity of the mass spectrometer. Reinjection of another  aliquot of the sample extract will not resolve the problem. Additional cleanup of the extract may be required to remove the interferences.

    - All CDDs/CDFs and labeled com- pounds in the CS1 standard shall  be  within the QC limits in Table 9  for  their  respective ion abundance ratios; otherwise, the mass spectrometer shall be adjusted and this test repeated until the m/z ratios fall within the limits specified. If the adjustment alters the resolution of the mass spectrometer, resolu- tion shall be verified (Section 10.1.2) prior to repeat  of  the  test.

#### 40 CFR Ch. I (7–1–17 Edition)

    - Verify that the HRGC/HRMS instru- ment meets the minimum levels in Table 2. The peaks representing the CDDs/CDFs and labeled compounds in the CS1 calibration standard must have signal-to-noise ratios (S/

N) greater than or equal to  10.0.  Otherwise, the mass spectrometer shall be adjusted and this test repeated  until  the  minimum  levels in Table 2 are met.

    - The absolute retention time of 13C12- 1,2,3,4–TCDD (Section 7.12) shall exceed 25.0 minutes on the DB–5 column, and the reten- tion   time   of   13C12-1,2,3,4–TCDD   shall   exceed

15.0 minutes on the DB–225 column; other- wise, the GC temperature program shall be adjusted and this test repeated until the above-stated minimum retention time cri- teria are met.

2010.3   Retention-Time   Windows—Analyze the window defining mixtures (Section 7.15) using the optimized temperature program in Section 10.1. Table 5 gives the elution order (first/last) of the  window-defining  com- pounds. If 2,3,7,8-TCDD and 2,3,7,8-TCDF only are  to  be  analyzed,  this  test  is  not  required.

  - Isomer Specificity.

    - Analyze the isomer specificity test standards (Section 7.15) using the procedure in Section 14 and the optimized  conditions for sample analysis (Section 10.1.1).

    - Compute the percent valley between the GC peaks that elute most closely to the 2,3,7,8-TCDD and TCDF isomers, on their re- spective columns, per Figures 6 and 7.

    - Verify that the height of the valley between the most closely eluted isomers and the 2,3,7,8-substituted isomers is less than 25% (computed as 100 x/y in Figures 6 and 7). If the valley exceeds 25%, adjust the analyt- ical conditions and repeat the test or replace the   GC   column   and   recalibrate   (Sections

10.1.2 through 10.7).

  - Calibration by Isotope Dilution—Iso- tope dilution calibration is used for the 15 2,3,7,8-substituted CDDs/CDFs for which la- beled compounds are added to samples prior to extraction. The reference compound for each CDD/CDF compound is shown in Table 2.

    - A calibration curve encompassing the concentration range is prepared for each compound to be determined. The relative re- sponse (RR) (labeled to native) vs. concentra- tion in standard solutions is plotted or com- puted using a linear regression. Relative re- sponse is determined according to the proce- dures described below. Five calibration points are employed.

    - The response of each CDD/CDF rel- ative to its labeled analog  is  determined using the area responses of both the primary and secondary exact m/z’s specified in Table 8, for each calibration standard, as follows:

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1613

where:

## RR 

A1n A2n Cl

A1l A2l Cn

dure in Section 14 and the conditions in Sec- tion 10.1.1 and Table 2. Compute the response factor (RF) at each concentration.

10.6.3 Linearity—If the response factor (RF) for any compound is constant (less than 35% coefficient of variation) over the five-

A1n and A2n = The areas of the primary and secondary m/z’s for the CDD/CDF.

A1l and A2l = The areas of the primary and secondary m/z’s for the labeled com- pound.

Cl = The concentration of the labeled com- pound in the calibration standard (Table 4).

Cn = The concentration of the native com- pound in the calibration standard (Table 4).

10.5.3 To calibrate  the  analytical  system by isotope dilution, inject a volume of cali- bration  standards  CS1  through  CS5  (Section

7.13 and Table 4) identical to the volume cho- sen in Section 10.2, using the procedure in Section   14   and   the   conditions   in   Section

10.1.1 and Table 2. Compute the relative re- sponse (RR) at each concentration.

10.5.4 Linearity—If the relative response for any compound is constant (less than 20% coefficient of variation) over the five-point calibration range, an averaged relative re- sponse may be used for that compound; oth- erwise, the complete calibration curve for that compound shall be used over the five- point calibration range.

  - Calibration by Internal Standard— The internal standard method is applied to determination of 1,2,3,7,8,9-HxCDD (Section 17.1.2), OCDF (Section 17.1.1), the non 2,3,7,8- substituted compounds, and to the deter- mination of labeled compounds for intralaboratory statistics (Sections 9.4 and 15.5.4).

    - Response factors—Calibration re- quires the determination of response factors (RF) defined by the following equation:

A1s A2s Cis

## RF 

A1is A2is Cs

where:

A1s and A2s = The areas of the primary and secondary m/z’s for the CDD/CDF.

A1is and A2is = The areas of the primary and secondary m/z’s for the internal stand- ard.

Cis = The concentration of the internal stand- ard (Table 4).

Cs = The concentration of the compound in the calibration standard (Table 4).

NOTE: There is only one m/z for 37Cl4-2,3,7,8- TCDD. See Table 8.

    - To calibrate the analytical system by internal standard, inject 1.0 L or 2.0 L of calibration standards CS1 through CS5 (Section  7.13  and  Table  4)  using  the  proce-

point calibration range, an averaged re- sponse factor may be used for that com- pound; otherwise, the complete calibration curve for that compound shall be used over the five-point range.

  - Combined Calibration—By using cali- bration solutions (Section 7.13 and Table 4) containing the  CDDs/CDFs  and  labeled  com- pounds and the internal standards, a  single set of analyses can be used to produce cali- bration curves for the isotope dilution and internal standard methods. These curves are verified each shift (Section 15.3) by analyzing the calibration verification standard (VER, Table 4). Recalibration is required if  any  of the calibration verification criteria (Section 15.3) cannot be met.

  - Data Storage—MS data shall be col- lected, recorded, and stored.

    - Data  acquisition—The  signal   at each exact m/z shall be collected repetitively throughout the monitoring period and stored on a mass storage device.

    - Response factors and multipoint calibrations—The data system shall  be  used to record and maintain lists of response fac- tors (response ratios for isotope dilution) and multipoint calibration curves.  Computations of relative standard deviation (coefficient of variation) shall be used to test calibration linearity. Statistics on initial performance (Section 9.2) and ongoing performance (Sec- tion 15.5) should be computed and main- tained, either on the instrument data sys- tem, or on a separate computer system.

11.0    Sample Preparation

  - Sample preparation involves modi- fying the physical form of the sample so that the CDDs/CDFs can be extracted efficiently. In general, the samples must be in a liquid form or in the form of finely divided solids in order for efficient extraction to take place. Table 10 lists the phases and suggested quan- tities for extraction of various sample mat- rices.

For samples known or expected to contain high levels of the CDDs/CDFs, the smallest sample size representative of the entire sam- ple should be used (see Section 17.5).

For all samples, the blank and IPR/OPR aliquots must be processed through the same steps as the sample to check for contamina- tion and losses in the preparation processes.

    - For samples that contain particles, percent solids and particle size are deter- mined using the procedures in Sections 11.2 and 11.3, respectively.

    - Aqueous samples—Because CDDs/ CDFs  may  be  bound  to  suspended  particles,

#### Pt. 136, App. A, Meth. 1613

the preparation of aqueous samples is de- pendent on the solids content of the sample.

      - Aqueous samples visibly absent particles are prepared per Section 11.4 and extracted directly using the separatory fun- nel or SPE techniques in Sections 12.1 or 12.2, respectively.

      - Aqueous samples containing visi- ble particles and containing one percent sus- pended solids or less are prepared using the procedure in Section 11.4. After preparation, the sample is extracted directly using the SPE technique in 12.2 or filtered per Section

11.4.3. After filtration, the particles  and  fil- ter are extracted using the SDS procedure in Section 12.3 and the filtrate  is  extracted using the separatory funnel procedure in Section 12.1.

      - For aqueous samples containing greater than one percent solids, a sample ali- quot sufficient to provide 10 g of dry solids is used, as described in Section 11.5.

    - Solid samples  are  prepared  using the procedure described in Section 11.5 fol- lowed by extraction via  the  SDS  procedure in Section 12.3.

    - Multiphase samples—The phase(s) containing the CDDs/CDFs is separated from

#### 40 CFR Ch. I (7–1–17 Edition)

the non-CDD/CDF phase using pressure fil- tration and centrifugation, as described in Section 11.6. The CDDs/CDFs will be in the organic phase in a multiphase sample in which an organic phase exists.

    - Procedures for grinding, homogeni- zation, and blending of  various  sample phases are given in Section 11.7.

    - Tissue samples—Preparation proce- dures for fish and other tissues are given in Section 11.8.

  - Determination of Percent Suspended Solids.

NOTE: This aliquot is used for determining the solids content of the sample, not for de- termination  of  CDDs/CDFs.

    - Aqueous liquids and multi-phase samples consisting of mainly an aqueous phase.

      - Dessicate and weigh a GF/D filter (Section 6.5.3) to three significant figures.

      - Filter 10.0 0.02 mL of well-mixed sample through the filter.

      - Dry the filter a minimum  of  12 hours at 110 5 C and cool in a dessicator.

      - Calculate percent solids as fol- lows:

## % solids weight of sample aliquot after drying (g) weight of filter (g) 100

10 g

    - Non-aqueous liquids, solids, semi- solid samples, and multi-phase samples in which the main phase is not aqueous; but not tissues.

      - Weigh 5–10 g of sample to three significant figures in a tared beaker.

      - Dry a minimum of 12 hours at 110

5 C, and cool in a dessicator.

      - Calculate   percent   solids   as   fol- lows:

## % solids weight of sample aliquot after drying   100 weight of sample aliquot before drying

  - Determination of Particle Size.

    - Spread the dried sample from Sec- tion 11.2.2.2 on a piece of filter paper or alu- minum foil in a fume hood or glove box.

    - Estimate the size of the particles  in the sample. If  the  size  of  the  largest  particles is greater than 1  mm,  the  particle  size  must be reduced to 1 mm or less prior  to  extrac- tion using the procedures in Section 11.7.

11.4 Preparation of Aqueous Samples Con- taining 1% Suspended Solids or Less.

11.4.1 Aqueous samples visibly absent par- ticles are prepared per the procedure below and extracted directly using the separatory funnel or SPE techniques in Sections 12.1 or

12.2, respectively. Aqueous samples con- taining visible particles and one percent sus- pended solids or less are prepared using the procedure below and extracted using either the SPE technique in Section 12.2 or further prepared using the filtration procedure in Section 11.4.3. The filtration procedure is fol- lowed by SDS extraction of the filter and particles (Section 12.3) and separatory funnel extraction of the filtrate (Section 12.1). The SPE procedure is followed by SDS extraction of the filter and disk.

    - Preparation    of    sample    and    QC aliquots.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1613

      - Mark the original level of the sample on the sample bottle for reference. Weigh the sample plus bottle to 1.

      - Spike 1.0 mL of the diluted la- beled-compound spiking solution (Section 7.10.3) into the sample bottle. Cap the bottle and mix the sample by  careful  shaking. Allow the sample to equilibrate for one to two hours, with occasional shaking.

      - For each sample or sample batch (to a maximum of 20 samples) to be extracted during the same 12-hour shift, place two 1.0 L aliquots of reagent water in clean sample bottles or flasks.

      - Spike 1.0 mL of the diluted la- beled-compound spiking solution (Section 7.10.3) into both reagent water aliquots. One of these aliquots will serve as the method blank.

      - Spike 1.0 mL of the PAR standard (Section 7.14) into the remaining reagent water aliquot. This aliquot will serve as the OPR (Section 15.5).

      - If SPE is to be used, add 5 mL of methanol to the sample, cap and shake the sample to mix thoroughly, and proceed to Section 12.2 for extraction. If  SPE  is  not  to be used, and the sample is visibly absent par- ticles, proceed to Section 12.1 for extraction. If SPE is not to be used and the sample con- tains visible particles, proceed to the fol- lowing section for filtration of particles.

    - Filtration of particles.

      - Assemble a Buchner funnel (Sec- tion 6.5.5) on top of a clean filtration flask. Apply vacuum to the flask, and pour the en- tire contents of the sample bottle through a glass-fiber filter (Section 6.5.6) in the Buchner funnel, swirling the sample remain- ing in the bottle to suspend any particles.

      - Rinse the sample bottle twice with approximately 5 mL portions of reagent water to transfer any  remaining  particles onto  the  filter.

      - Rinse any particles off the sides of the Buchner funnel with small quantities of reagent water.

      - Weigh the empty sample bottle to

1 g. Determine the weight of the sample by difference. Save the bottle for further use.

      - Extract the filtrate using the separatory funnel procedure in Section 12.1.

      - Extract the filter containing the particles using the SDS procedure in Section 12.3.

  - Preparation of Samples Containing Greater Than 1% Solids.

    - Weigh a well-mixed aliquot of each sample (of the same  matrix  type)  sufficient to provide 10 g of dry solids (based on the sol- ids determination in Section  11.2)  into  a clean beaker or glass jar.

    - Spike 1.0 mL of the diluted labeled compound spiking solution (Section 7.10.3) into the sample.

    - For each sample or sample batch (to a  maximum  of  20  samples)  to  be  extracted

during the same 12-hour shift, weigh two 10 g aliquots of the appropriate reference matrix (Section 7.6) into clean beakers or glass jars.

    - Spike 1.0 mL of the diluted labeled compound spiking solution (Section 7.10.3) into each reference matrix aliquot. One ali- quot  will  serve  as  the  method  blank.  Spike

1.0 mL of the PAR standard (Section 7.14) into the other reference matrix aliquot. This aliquot will serve as the OPR (Section 15.5).

    - Stir or tumble and equilibrate the aliquots for one to two hours.

    - Decant excess water. If necessary to remove water, filter the sample through a glass-fiber filter and discard the aqueous liq- uid.

    - If particles >1mm are present in the sample (as determined in Section 11.3.2), spread the sample on clean aluminum foil in a hood. After the sample is dry, grind to re- duce the particle size (Section 11.7).

    - Extract the sample and QC aliquots using the SDS procedure in Section 12.3.

  - Multiphase Samples.

    - Using the percent solids determined in Section 11.2.1 or 11.2.2, determine the vol- ume of sample that will provide 10 g of sol- ids, up to 1 L of sample.

    - Pressure filter the amount of sam- ple determined in Section 11.6.1 through Whatman GF/D glass-fiber filter paper (Sec- tion 6.5.3). Pressure filter the blank and OPR aliquots through GF/D papers also. If nec- essary to separate the phases and/or  settle the solids, centrifuge these aliquots prior to filtration.

    - Discard any aqueous phase (if present). Remove any non-aqueous liquid present and reserve the maximum amount filtered from the sample (Section 11.6.1) or 10 g, whichever is less, for combination  with the solid phase (Section 12.3.5).

    - If particles >1mm are present in the sample (as determined in Section 11.3.2) and the sample is capable of being dried, spread the sample and QC aliquots on clean alu- minum foil in a hood. After the aliquots are dry or if the sample cannot be dried, reduce the particle size using the procedures in Sec- tion 11.7 and extract the reduced particles using the SDS procedure in Section 12.3. If particles >1mm are not present, extract the particles and filter in the sample and QC aliquots directly using the SDS procedure in Section 12.3.

  - Sample grinding, homogenization, or blending—Samples with particle sizes  great- er than 1 mm (as determined in  Section 11.3.2) are subjected to grinding, homogeni- zation, or blending. The method of reducing particle size to less than 1 mm is matrix-de- pendent. In general, hard particles can be re- duced by grinding with a mortar and pestle. Softer particles can be  reduced  by  grinding in a Wiley mill or meat grinder, by homog- enization,  or  in  a  blender.

#### Pt. 136, App. A, Meth. 1613

    - Each size-reducing preparation pro- cedure on each matrix shall be verified by running the tests in Section 9.2 before the procedure is employed routinely.

    - The grinding, homogenization, or blending procedures shall be carried out in a glove box or fume hood to prevent particles from contaminating the work environment.

    - Grinding—Certain papers and pulps, slurries, and amorphous solids  can  be  ground in a Wiley mill  or  heavy  duty  meat  grinder. In some cases, reducing the temperature  of the sample to freezing or to dry ice or liquid nitrogen temperatures can aid in the  grind- ing process. Grind the sample aliquots from Section 11.5.7 or 11.6.4 in a clean grinder. Do not allow the sample temperature  to  exceed 50 C. Grind the blank and reference matrix aliquots  using  a  clean  grinder.

    - Homogenization or blending—Par- ticles that are not ground effectively, or par- ticles greater than 1 mm in size  after  grind- ing, can often  be  reduced  in  size  by  high speed homogenization or blending. Homog- enize and/or blend the particles or filter from Section 11.5.7 or 11.6.4 for the sample, blank, and  OPR  aliquots.

    - Extract the aliquots using the SDS procedure in Section 12.3.

  - Fish and Other Tissues—Prior to processing tissue samples, the laboratory must determine the exact tissue to be ana- lyzed. Common requests for analysis of fish tissue include whole fish—skin on, whole fish—skin removed, edible  fish  fillets (filleted in the field or by the laboratory), specific organs, and other portions. Once the appropriate tissue has been determined, the sample must be homogenized.

    - Homogenization.

      - Samples are homogenized while still frozen, where practical. If the labora- tory must  dissect  the whole  fish  to  obtain the appropriate tissue for analysis, the un- used tissues may be rapidly refrozen and stored in a clean glass jar for subsequent use.

      - Each analysis requires 10 g of tis- sue (wet weight). Therefore, the laboratory should homogenize at least 20 g of tissue to allow for re-extraction of a second aliquot of the same homogenized sample, if re-analysis is required. When whole fish analysis is nec- essary, the entire fish is homogenized.

      - Homogenize the sample in a tissue homogenizer (Section 6.3.3) or grind in a meat grinder (Section 6.3.4). Cut tissue too large to  feed  into  the grinder  into  smaller pieces. To assure homogeneity, grind three times.

      - Transfer approximately 10 g (wet weight) of homogenized tissue to a clean, tared, 400–500 mL beaker. For the alternate HCl digestion/extraction, transfer the  tissue to a clean, tared 500–600 mL wide-mouth bot- tle. Record the weight to the nearest 10 mg.

      - Transfer the remaining homog- enized    tissue    to    a    clean    jar    with    a

#### 40 CFR Ch. I (7–1–17 Edition)

fluoropolymer-lined lid. Seal the jar  and store the tissue at <¥10 C. Return  any  tis- sue that was not homogenized to its original container and store at <¥10 C.

    - QC aliquots.

      - Prepare a method blank by adding approximately 10 g of the oily  liquid  ref- erence matrix (Section 7.6.4) to a 400–500 mL beaker. For the alternate HCl digestion/ex- traction, add the reference matrix to a  500– 600 mL wide-mouth  bottle.  Record  the weight to the nearest 10 mg.

      - Prepare a precision and recovery aliquot by adding approximately 10 g of the oily liquid reference matrix (Section 7.6.4) to a separate 400–500 mL beaker or wide-mouth bottle, depending on the extraction proce- dure to be used. Record the weight to the nearest 10 mg. If the initial precision and re- covery test is to be performed, use four aliquots; if the ongoing precision and recov- ery test is to be performed, use a single ali- quot.

    - Spiking

      - Spike 1.0 mL of the labeled com- pound spiking solution (Section 7.10.3) into the sample, blank, and OPR aliquot.

      - Spike 1.0 mL of the PAR standard (Section 7.14) into the OPR aliquot.

11.8.4 Extract the  aliquots  using  the pro- cedures in Section 12.4.

12.0   Extraction and Concentration

Extraction procedures include separatory funnel (Section 12.1) and solid phase (Section 12.2) for aqueous liquids; Soxhlet/Dean-Stark (Section 12.3) for solids, filters, and  SPE disks; and Soxhlet extraction (Section 12.4.1) and HCl digestion (Section 12.4.2) for tissues. Acid/base back-extraction (Section 12.5) is used for initial cleanup of extracts.

Macro-concentration procedures include rotary evaporation (Section 12.6.1), heating mantle (Section 12.6.2), and Kuderna-Danish (K-D) evaporation (Section 12.6.3). Micro- concentration uses nitrogen blowdown (Sec- tion 12.7).

  - Separatory funnel extraction of fil- trates and of aqueous samples visibly absent particles.

    - Pour the spiked sample (Section 11.4.2.2) or filtrate (Section 11.4.3.5) into a 2 L separatory funnel. Rinse the bottle or flask twice with 5 mL of reagent water and add these rinses to the separatory funnel.

    - Add 60 mL methylene chloride to the empty sample bottle  (Section  12.1.1), seal, and shake 60 seconds to rinse the inner surface. Transfer the solvent to the sepa- ratory funnel, and extract the sample by shaking the funnel for two minutes with periodic venting. Allow the organic layer to separate from the aqueous phase for a min- imum of 10 minutes. If an emulsion  forms and is more than one-third the volume of the solvent layer, employ mechanical techniques to  complete  the  phase  separation  (see  note

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1613

below). Drain the methylene chloride extract through a solvent-rinsed glass funnel ap- proximately one-half full of granular anhy- drous sodium sulfate (Section 7.2.1) sup- ported on clean glass-fiber paper into a sol- vent-rinsed concentration device (Section 12.6).

NOTE: If an emulsion forms, the analyst must employ mechanical techniques to com- plete the phase separation. The optimum technique depends upon the sample, but may include stirring, filtration  through  glass wool, use of phase separation paper, cen- trifugation, use of an ultrasonic bath  with ice, addition of NaCl, or other physical meth- ods. Alternatively, solid-phase or other ex- traction techniques may be used to prevent emulsion formation. Any alternative tech- nique is acceptable so long as the require- ments in Section 9 are met.

Experience with aqueous samples high in dissolved organic materials (e.g., paper mill effluents) has shown that acidification of the sample prior to extraction may reduce the formation of emulsions. Paper industry methods suggest that the addition of up to

400 mL of ethanol to a 1 L  effluent  sample may also reduce emulsion formation. How- ever, studies by EPA suggest that the effect may be a result of sample dilution, and that the addition of reagent water may serve the same function. Mechanical techniques may still be necessary to complete the phase sep- aration. If either acidification or addition of ethanol is utilized, the laboratory must per- form  the  startup  tests  described  in  Section

9.2 using the same techniques.

    - Extract the water sample two more times with 60 mL portions of methylene chloride. Drain each portion through the so- dium sulfate into the concentrator. After the third extraction, rinse the separatory funnel with at least 20 mL of methylene  chloride, and drain this rinse through the sodium sul- fate into the concentrator.  Repeat  this  rinse at least twice. Set aside the funnel with so- dium sulfate if the extract is to be combined with the extract from the particles.

    - Concentrate the extract using  one of the macro-concentration procedures in Section 12.6.

      - If the extract is from a sample visibly absent particles (Section 11.1.2.1), ad- just the final volume of the concentrated ex- tract to approximately 10 mL with hexane, transfer to a 250 mL separatory funnel, and back-extract using the procedure in Section 12.5.

      - If the extract is from the aqueous filtrate (Section 11.4.3.5), set aside the con- centration apparatus for addition of the SDS extract from the particles (Section 12.3.9.1.2).

12.2  SPE  of  Samples  Containing   Less Than 1% Solids (References 19–20).

12.2.1    Disk preparation.

      - Place an SPE disk on the base of the filter holder (Figure 4) and wet with tol- uene. While holding a GMF 150 filter above the SPE disk with tweezers, wet the filter with toluene and lay the filter on the SPE disk, making sure that air is not trapped be- tween the filter and disk. Clamp the  filter and SPE disk between the 1 L glass reservoir and the vacuum filtration flask.

      - Rinse the sides of  the  filtration flask with approx 15 mL of toluene using a squeeze bottle or syringe. Apply vacuum mo- mentarily until a few drops appear at the drip tip. Release the vacuum and allow the filter/disk to soak for approx one minute. Apply vacuum and draw all of the toluene through the filter/disk. Repeat the wash step with approx 15 mL of acetone and allow the filter/disk to air dry.

      - Re-wet the filter/disk with ap- proximately 15 mL of methanol, allowing the filter/disk to soak for approximately one minute. Pull the methanol through the fil- ter/disk using the vacuum, but retain a layer of methanol approximately 1 mm thick  on the filter. Do not allow the disk to go  dry from this point until the end of the extrac- tion.

      - Rinse the filter/disk with two 50- mL portions of reagent water by adding the water to the reservoir and pulling most through, leaving a layer of water on the sur- face of the filter.

    - Extraction.

      - Pour the spiked sample (Section 11.4.2.2), blank (Section 11.4.2.4), or IPR/OPR aliquot (Section 11.4.2.5) into the reservoir and turn on the vacuum to begin the extrac- tion. Adjust the vacuum to complete the ex- traction in no less than 10 minutes. For sam- ples containing a high concentration of par- ticles (suspended solids), filtration  times may be eight hours or longer.

      - Before all of the sample has been pulled through the filter/disk, rinse the sam- ple bottle with approximately 50 mL of rea- gent water to remove any solids, and pour into the reservoir. Pull through the filter/ disk. Use additional reagent  water  rinses until all visible solids are removed.

      - Before all of the sample and rinses have been pulled through the  filter/disk, rinse the sides of the reservoir with small portions of reagent water.

      - Allow the filter/disk to dry, then remove the filter and disk and place in a glass Petri dish. Extract the filter and  disk per Section 12.3.

  - SDS Extraction of Samples Con- taining Particles, and of Filters and/or Disks.

    - Charge a clean extraction thimble (Section 6.4.2.2) with 5.0 g of 100/200 mesh sili- ca (Section 7.5.1.1) topped with 100 g of quartz sand (Section 7.3.2).

#### Pt. 136, App. A, Meth. 1613

NOTE: Do not disturb the silica layer throughout the extraction process.

    - Place the thimble in a clean extrac- tor. Place 30–40 mL of toluene in the receiver and 200–250 mL of toluene in the flask.

    - Pre-extract the glassware by heat- ing the flask until the toluene is boiling. When properly adjusted, one to two drops of toluene will fall per second from the con- denser tip into the receiver. Extract the ap- paratus for a minimum of three hours.

    - After pre-extraction, cool and dis- assemble the  apparatus.  Rinse  the  thimble with toluene and allow to air dry.

    - Load the wet sample, filter, and/or disk from Section 11.4.3.6, 11.5.8, 11.6.4, 11.7.3, 11.7.4, or 12.2.2.4 and any nonaqueous liquid from Section 11.6.3 into the thimble and manually mix into  the  sand  layer  with  a clean metal spatula, carefully breaking up any large lumps of sample.

    - Reassemble the pre-extracted SDS apparatus, and add a fresh charge of toluene to the receiver and reflux flask. Apply power to the heating mantle to begin refluxing. Ad- just the reflux rate to match the rate of per- colation through the sand and silica beds until water removal lessens  the  restriction to toluene flow. Frequently check the appa- ratus for foaming during the first two hours of extraction. If foaming occurs, reduce the reflux rate until foaming subsides.

    - Drain  the  water  from   the   receiver at one to two  hours  and  eight  to  nine  hours, or sooner if the receiver  fills  with  water. Reflux the sample for a total of 16–24 hours. Cool and disassemble the apparatus. Record the  total  volume  of  water  collected.

    - Remove the distilling flask. Drain the water from the Dean-Stark receiver and add any toluene in the receiver to the ex- tract in the flask.

    - Concentrate the extract using  one of the macro-concentration procedures in Section 12.6 per the following:

      - Extracts from the particles in an aqueous sample containing less than 1% sol- ids (Section 11.4.3.6).

        - Concentrate the extract to ap- proximately 5 mL using the rotary evapo- rator or heating mantle procedures in Sec- tion 12.6.1 or 12.6.2.

        - Quantitatively transfer the ex- tract through the sodium sulfate (Section 12.1.3) into the apparatus that was set aside (Section 12.1.4.2) and reconcentrate to the level of the toluene.

        - Adjust to approximately 10 mL with hexane, transfer to a 250 mL separatory funnel, and proceed with back-extraction (Section 12.5).

12.3.9.2  Extracts from particles (Sections

11.5 through  11.6)  or  from  the  SPE  filter  and disk (Section 12.2.2.4)—Concentrate to ap- proximately 10 mL using the rotary evapo- rator   or   heating   mantle   (Section   12.6.1   or

#### 40 CFR Ch. I (7–1–17 Edition)

12.6.2), transfer to a 250 mL separatory fun- nel, and proceed with back-extraction (Sec- tion 12.5).

  - Extraction of Tissue—Two procedures are provided for tissue extraction.

    - Soxhlet extraction (Reference 21).

      - Add 30–40 g of powdered anhydrous sodium sulfate to each of the beakers  (Sec- tion 11.8.4) and mix thoroughly. Cover the beakers with aluminum foil and allow to equilibrate for 12–24 hours. Remix prior to extraction  to  prevent  clumping.

      - Assemble and pre-extract the Soxhlet apparatus per Sections  12.3.1 through 12.3.4, except use the methylene chloride:hexane (1:1) mixture for the pre-ex- traction and rinsing and  omit  the  quartz sand. The Dean-Stark  moisture  trap  may also be omitted, if desired.

      - Reassemble the pre-extracted Soxhlet apparatus and add a fresh charge of methylene chloride:hexane  to  the  reflux flask.

      - Transfer the sample/sodium sul- fate mixture (Section 12.4.1.1) to the Soxhlet thimble, and install the thimble in the Soxh- let apparatus.

      - Rinse the beaker with several por- tions of solvent mixture and add to the thim- ble. Fill the thimble/receiver with solvent. Extract for 18–24 hours.

      - After extraction, cool and dis- assemble the apparatus.

      - Quantitatively transfer the ex- tract to a macro-concentration device (Sec- tion 12.6), and concentrate to near dryness. Set aside the concentration apparatus for re- use.

      - Complete the removal of the sol- vent using the nitrogen blowdown procedure (Section 12.7) and a  water  bath  temperature of 60 C. Weigh the receiver, record  the weight, and return the receiver to the blow- down apparatus, concentrating the residue until  a  constant  weight  is  obtained.

      - Percent lipid determination—The lipid content is determined by extraction of tissue with the same solvent system (meth- ylene chloride:hexane) that was used in EPA’s National Dioxin Study  (Reference  22) so that lipid contents are consistent with that  study.

        - Redissolve the residue in the re- ceiver in hexane and spike 1.0 mL of the cleanup standard (Section 7.11) into the solu- tion.

        - Transfer the residue/hexane to the anthropogenic isolation column (Section 13.7.1) or bottle for the acidified silica gel batch cleanup (Section 13.7.2), retaining the boiling chips in the concentration apparatus. Use several rinses to assure that all material is transferred. If necessary, sonicate or heat the receiver slightly to assure that all mate- rial is re-dissolved. Allow the receiver to dry. Weigh the receiver and boiling chips.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1613

        - Calculate the lipid  content  to the nearest three significant figures as fol- lows:

Percent lipid = Weight of residue (g) 100

Weight of tissue (g)

        - It is not necessary to determine the lipid content of the blank, IPR, or OPR aliquots.

    - HCl digestion/extraction and con- centration (References 23–26).

      - Add 200 mL of 6 N HCl and 200 mL of methylene chloride:hexane (1:1) to the sample and QC aliquots (Section 11.8.4).

      - Cap and shake each bottle one to three times. Loosen the cap in a hood to vent excess pressure. Shake each bottle for 10–30 seconds  and  vent.

      - Tightly cap and place on shaker. Adjust the shaker action and speed so that the acid, solvent, and tissue are in constant motion. However, take care to avoid such violent action that the bottle may be dis- lodged from the shaker. Shake for 12–24 hours.

      - After digestion, remove the bot- tles from the shaker. Allow the bottles to stand so that the solvent and acid layers sep- arate.

      - Decant the solvent through a glass funnel with glass-fiber filter (Sections 6.5.2 through 6.5.3) containing approximately 10 g of granular anhydrous sodium sulfate (Sec- tion 7.2.1) into a macro-concentration appa- ratus (Section 12.6). Rinse the contents  of the bottle with two 25 mL portions of hexane and pour through the sodium sulfate into the apparatus.

      - Concentrate the solvent to near dryness using a macro-concentration proce- dure (Section 12.6).

      - Complete the removal of the sol- vent using the nitrogen blowdown apparatus (Section 12.7) and a  water  bath  temperature of 60 C. Weigh the receiver, record  the weight, and return the receiver to the blow- down apparatus, concentrating the residue until  a  constant  weight  is  obtained.

      - Percent lipid determination—The lipid content is determined in the same sol- vent  system   [methylene   chloride:hexane (1:1)] that was used in EPA’s National Dioxin Study (Reference 22) so that lipid  contents are  consistent  with  that  study.

        - Redissolve the residue in the re- ceiver in hexane and spike 1.0 mL of the cleanup standard (Section 7.11) into the solu- tion.

        - Transfer the residue/hexane  to the narrow-mouth 100–200 mL bottle retain- ing the boiling chips in the receiver. Use  sev- eral rinses to assure that all material is transferred, to a maximum hexane volume of approximately 70 mL. Allow the receiver to dry.  Weigh  the  receiver  and  boiling  chips.

        - Calculate the percent lipid per Section 12.4.1.9.3. It is not necessary to deter- mine the lipid content of the blank, IPR, or OPR aliquots.

12.4.2.9 Clean up the extract per Section 13.7.3.

  - Back-Extraction with Base and Acid.

    - Spike 1.0 mL of the cleanup stand- ard (Section 7.11) into the separatory funnels containing the sample and QC extracts from Section 12.1.4.1, 12.3.9.1.3, or 12.3.9.2.

    - Partition the extract against  50  mL of potassium hydroxide solution (Section 7.1.1). Shake for two minutes with periodic venting into a hood. Remove and discard the aqueous layer. Repeat the base washing until no color is visible in the aqueous layer, to a maximum of four washings. Minimize con- tact time between the  extract  and  the  base to prevent degradation of the CDDs/CDFs. Stronger potassium hydroxide solutions may be employed for back-extraction,  provided that the laboratory meets the  specifications for labeled compound recovery and dem- onstrates acceptable performance using the procedure in Section 9.2.

    - Partition the extract against  50  mL of sodium chloride solution (Section 7.1.4) in the same way as with base. Discard the aque- ous layer.

    - Partition the extract against  50  mL of sulfuric acid (Section 7.1.2) in the same way as with base. Repeat the acid washing until no color is visible in the aqueous layer, to a maximum of four washings.

    - Repeat the partitioning against so- dium chloride solution and discard the aque- ous layer.

    - Pour each extract through a drying column containing 7–10 cm of granular anhy- drous sodium sulfate (Section 7.2.1). Rinse the separatory funnel with 30–50 mL of sol- vent, and pour through the drying column. Collect each extract in a round-bottom flask. Re-concentrate the sample and QC aliquots per Sections 12.6 through 12.7, and clean up the samples and QC aliquots per Section 13.

  - Macro-Concentration—Extracts in toluene are concentrated using a rotary evaporator or a heating mantle; extracts in methylene chloride or hexane are con- centrated using a rotary evaporator, heating mantle, or Kuderna-Danish apparatus.

    - Rotary evaporation—Concentrate the extracts in separate  round-bottom flasks.

      - Assemble the rotary evaporator according  to  manufacturer’s  instructions, and warm the water bath to 45 C. On a daily basis, preclean the rotary evaporator by con- centrating 100 mL of clean extraction sol- vent through the system. Archive both the concentrated solvent and the solvent in the catch flask for a contamination check if nec- essary. Between samples, three 2–3 mL aliquots of solvent should be rinsed down the feed tube into a waste beaker.

#### Pt. 136, App. A, Meth. 1613

      - Attach the round-bottom flask containing the sample extract to the rotary evaporator. Slowly apply vacuum to the sys- tem, and begin rotating the sample flask.

      - Lower the flask into the  water bath, and adjust the speed of  rotation  and the temperature as required to complete con- centration in 15–20 minutes. At the proper rate of  concentration,  the  flow  of  solvent into the receiving flask will  be  steady,  but no bumping or visible boiling of the  extract will  occur.

NOTE: If the rate of concentration is too fast, analyte loss may occur.

      - When the liquid in the concentra- tion flask has reached an apparent volume of approximately 2 mL, remove the flask  from the water bath and stop the rotation. Slowly and carefully admit air into the system. Be sure not to open the valve  so  quickly  that the sample is blown out of  the  flask.  Rinse the feed tube with approximately 2 mL of solvent.

      - Proceed to Section 12.6.4 for prepa- ration for back-extraction or micro-con- centration and solvent exchange.

    - Heating mantle—Concentrate the extracts in separate round-bottom flasks.

      - Add one or two clean boiling chips to the round-bottom flask, and attach a three-ball macro Snyder column. Prewet the column by adding approximately 1 mL of sol- vent through the top. Place the round-bot- tom flask in a heating mantle, and apply heat as required to complete the concentra- tion in 15–20 minutes. At the proper rate of distillation, the balls of the column will ac- tively chatter, but the chambers  will  not flood.

      - When the liquid has reached an ap- parent volume of approximately 10 mL, re- move the round-bottom flask from the heat- ing mantle and allow the solvent to  drain and cool for at least 10 minutes. Remove the Snyder column and rinse the glass joint into the receiver with small portions of solvent.

      - Proceed to Section 12.6.4 for prepa- ration for back-extraction or micro-con- centration and solvent exchange.

    - Kuderna-Danish (K-D)—Concentrate the extracts in separate 500 mL K-D flasks equipped with 10 mL concentrator tubes. The K-D technique is used for solvents such as methylene chloride and hexane. Toluene is difficult to concentrate using the K-D tech- nique unless a water bath fed by a steam generator is used.

      - Add one to two clean boiling chips to the receiver. Attach a three-ball macro Snyder column. Prewet the column by  add- ing approximately 1 mL of solvent  through the top. Place the K-D apparatus in a hot water bath so that the entire lower rounded surface of the flask is bathed with steam.

      - Adjust the vertical position of the apparatus and the water temperature as re-

#### 40 CFR Ch. I (7–1–17 Edition)

quired to complete the concentration in 15–20 minutes. At the proper rate of  distillation, the balls of the column will actively chatter but the chambers will not flood.

      - When the liquid has reached an ap- parent volume of 1 mL, remove the K-D ap- paratus from the bath and allow the solvent to drain and cool for at least 10 minutes. Re- move the Snyder column and rinse the flask and its lower  joint  into  the  concentrator tube with 1–2 mL of solvent. A 5 mL syringe is recommended for this operation.

      - Remove the three-ball Snyder col- umn, add a fresh boiling chip, and attach a two-ball micro Snyder column to the concen- trator tube. Prewet the column by adding approximately 0.5 mL of solvent through the top. Place the apparatus in the hot water bath.

      - Adjust the vertical position and the water temperature as required to com- plete the concentration in 5–10 minutes. At the proper rate of distillation, the  balls  of the column will actively chatter but the chambers will not flood.

      - When the liquid reaches an appar- ent volume of 0.5 mL, remove the apparatus from the water bath and allow to drain  and cool for at least 10 minutes.

      - Proceed to 12.6.4 for preparation for back-extraction or micro-concentration and solvent exchange.

    - Preparation for back-extraction or micro-concentration and solvent exchange.

      - For back-extraction (Section 12.5), transfer the extract to a 250 mL separatory funnel. Rinse the concentration vessel  with small portions of hexane, adjust the hexane volume in the separatory funnel to 10–20 mL, and  proceed  to   back-extraction   (Section 12.5).

      - For determination of the weight of residue in the extract, or for clean-up proce- dures other than back-extraction, transfer the extract to a blowdown vial using two to three rinses of solvent. Proceed with micro- concentration and solvent exchange (Section 12.7).

  - Micro-Concentration and Solvent Ex- change.

    - Extracts to be subjected to GPC or HPLC cleanup are exchanged into methylene chloride. Extracts to be cleaned up using sili- ca gel, alumina, carbon, and/or Florisil are exchanged into hexane.

    - Transfer the vial containing the sample extract to a nitrogen blowdown de- vice. Adjust the flow of nitrogen so that the surface of the solvent is just visibly dis- turbed.

NOTE: A large vortex in the solvent may cause analyte loss.

    - Lower the vial into a 45 C water bath and continue concentrating.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1613

      - If the extract is to be con- centrated to dryness for weight determina- tion (Sections 12.4.1.8, 12.4.2.7, and 13.7.1.4), blow dry until a constant weight is obtained.

      - If the extract is to be con- centrated for injection into the GC/MS or the solvent is to be exchanged for extract clean- up, proceed as follows:

    - When the volume of the liquid is ap- proximately 100 L, add 2–3 mL of the desired solvent (methylene chloride for GPC and HPLC, or hexane for the other cleanups) and continue concentration to approximately 100

L. Repeat the addition of solvent and con- centrate once more.

    - If the extract is to be cleaned up by GPC, adjust the volume of the  extract  to  5.0 mL  with  methylene   chloride.   If   the   extract is to be cleaned up by HPLC, further con- centrate the extract to 30 L. Proceed with GPC or HPLC cleanup (Section 13.2 or 13.6, respectively).

    - If the extract is to be cleaned up by column chromatography (alumina, silica gel, Carbopak/Celite, or Florisil), bring the final volume to 1.0 mL with hexane. Proceed with column cleanups (Sections 13.3 through 13.5 and 13.8).

    - If the extract is to be concentrated for injection into the GC/MS (Section 14), quantitatively transfer the extract to a  0.3 mL conical vial for final concentration, rins- ing the larger vial with hexane and adding the rinse to the conical vial. Reduce the vol- ume to approximately 100 L. Add 10 L of nonane to the vial, and evaporate the solvent to the level of the nonane. Seal the vial and label with the sample number. Store in the dark at room temperature until ready for GC/MS analysis. If GC/MS analysis will not be performed on the same day, store the vial at <¥10 C.

13.0    Extract Cleanup

  - Cleanup may not be necessary for rel- atively clean samples (e.g., treated effluents, groundwater, drinking water). If particular circumstances require the use of a cleanup procedure, the analyst may use any or all of the procedures below or any other appro- priate procedure. Before using a cleanup pro- cedure, the analyst must demonstrate that the requirements of Section 9.2 can be met using the cleanup procedure. If only 2,3,7,8- TCDD and 2,3,7,8-TCDF are to be determined, the cleanup procedures may be optimized for isolation of these two compounds.

    - Gel permeation chromatography (Section 13.2) removes high molecular weight interferences that cause GC column perform- ance to degrade. It should be used for all soil and sediment extracts and may be used for water extracts that are expected to contain high molecular weight organic compounds (e.g.,  polymeric  materials,  humic  acids).

    - Acid, neutral, and basic silica gel (Section  13.3),  alumina  (Section  13.4),  and

Florisil (Section 13.8) are used to remove nonpolar and polar  interferences.  Alumina and Florisil are used to  remove chlorodiphenyl  ethers.

    - Carbopak/Celite (Section 13.5) is used to remove nonpolar interferences.

    - HPLC (Section 13.6) is used to pro- vide specificity for the 2,3,7,8-substituted and other CDD and CDF isomers.

    - The anthropogenic isolation  column (Section 13.7.1), acidified silica gel batch ad- sorption procedure (Section 13.7.2), and sul- furic acid and base back-extraction (Section 13.7.3) are used for removal of lipids from tis- sue samples.

  - Gel Permeation Chromatography (GPC).

    - Column packing.

      - Place 70–75 g of SX–3 Bio-beads (Section 6.7.1.1) in a 400–500 mL beaker.

      - Cover the beads with methylene chloride and allow to swell overnight (a min- imum of 12 hours).

      - Transfer the swelled beads to the column (Section 6.7.1.1) and pump solvent through the column, from bottom to top, at 4.5–5.5 mL/minute prior to connecting the column to the detector.

      - After purging the column with sol- vent for one to two hours, adjust the column head pressure to 7–10 psig and purge for four to five hours to remove air. Maintain a head pressure of 7–10 psig. Connect the  column  to the  detector  (Section  6.7.1.4).

    - Column calibration.

      - Load 5 mL of the calibration solu- tion (Section 7.4) into the sample loop.

      - Inject the calibration solution and record the signal from the detector. The elution pattern will be corn oil, bis(2-ethyl hexyl)phthalate, pentachlorophenol, pery- lene, and sulfur.

      - Set  the  ‘‘dump  time’’  to  allow

>85% removal of the corn oil and >85% col- lection of the phthalate.

      - Set the ‘‘collect time’’ to the peak minimum between perylene and sulfur.

      - Verify the calibration with the calibration solution after every 20 extracts. Calibration is verified if the recovery of the pentachlorophenol is greater than 85%. If calibration is not verified,  the  system  shall be recalibrated using the calibration solu- tion, and the previous 20 samples shall be re- extracted and cleaned up using the cali- brated  GPC  system.

    - Extract cleanup—GPC requires  that the column not be overloaded. The column specified in this method is designed  to  han- dle a maximum of 0.5 g of high molecular weight material in a 5 mL extract. If the  ex- tract is known or expected to contain more than 0.5 g, the extract is  split  into  aliquots for  GPC,  and  the  aliquots  are  combined  after

#### Pt. 136, App. A, Meth. 1613

elution from the column. The residue con- tent of the extract may be obtained gravi- metrically by evaporating the solvent from a 50 L aliquot.

      - Filter the extract or load through the filter holder (Section 6.7.1.3) to remove the particles. Load the 5.0 mL extract onto the column.

      - Elute the extract using the cali- bration data determined in Section 13.2.2. Collect the eluate in a clean 400–500 mL beaker.

      - Rinse the sample loading tube thoroughly with methylene chloride between extracts to prepare for the next sample.

      - If a particularly dirty extract is encountered, a 5.0 mL methylene chloride blank shall be run through the system to check for carry-over.

      - Concentrate the eluate per Sec- tions 12.6 and 12.7 for further cleanup or in- jection into the GC/MS.

  - Silica Gel Cleanup.

    - Place a glass-wool plug in a 15 mm ID chromatography column (Section 6.7.4.2). Pack the column bottom to top with: 1 g sili- ca gel (Section 7.5.1.1), 4 g basic silica gel (Section 7.5.1.3), 1 g silica gel, 8 g acid silica gel (Section 7.5.1.2), 2 g silica gel, and 4 g granular anhydrous sodium sulfate (Section 7.2.1). Tap the column to settle the adsorb- ents.

    - Pre-elute the column with 50–100 mL of hexane. Close the stopcock when the hexane is within 1 mm of the sodium sulfate. Discard the eluate. Check the column for channeling. If channeling is present, discard the column and prepare another.

    - Apply the concentrated extract to the column. Open the stopcock until the ex- tract  is  within  1  mm  of  the  sodium  sulfate.

    - Rinse the receiver  twice with  1 mL portions of hexane, and apply separately  to the column. Elute the CDDs/CDFs with  100 mL hexane, and collect the eluate.

    - Concentrate the eluate per Sections

12.6 and 12.7 for further cleanup or injection into the HPLC or GC/MS.

13.3.6 For extracts of  samples known to contain large quantities of other organic compounds (such as paper mill effluents), it may be advisable to increase the  capacity  of the silica gel column. This may be  accom- plished by  increasing  the  strengths  of  the acid and basic silica gels. The acid silica gel (Section 7.5.1.2) may be increased in strength to as much as 44% w/w (7.9 g sulfuric acid added to 10 g silica gel). The basic silica gel (Section 7.5.1.3) may be increased in strength to as much as 33% w/w (50 mL 1N NaOH added to 100 g silica gel), or the potassium silicate (Section 7.5.1.4) may be used.

NOTE: The use of stronger acid silica gel (44% w/w) may lead to charring of organic compounds in some extracts. The charred material  may  retain  some  of  the  analytes

#### 40 CFR Ch. I (7–1–17 Edition)

and lead to lower recoveries of CDDs/CDFs. Increasing the strengths of the acid and basic silica gel may also require different volumes of hexane than those specified above to elute the analytes off the column. There- fore, the performance of the method after such modifications must be verified by the procedure in Section 9.2.

  - Alumina Cleanup.

    - Place a glass-wool plug in a 15 mm ID chromatography column (Section 6.7.4.2).

    - If using acid alumina, pack the col- umn by adding 6 g acid alumina (Section 7.5.2.1). If using basic alumina, substitute 6 g basic alumina (Section 7.5.2.2). Tap the col- umn to settle the adsorbents.

    - Pre-elute the column  with 50–100 mL of hexane. Close the stopcock when the hexane is within 1 mm of the alumina.

    - Discard the eluate. Check the col- umn for channeling. If channeling is present, discard the column and prepare another.

    - Apply the concentrated extract  to the column. Open the stopcock until the ex- tract is within 1 mm of the alumina.

    - Rinse the receiver  twice with  1 mL portions of hexane and apply separately  to the column. Elute the interfering compounds with 100 mL hexane and discard the eluate.

    - The choice of eluting solvents will depend on the choice of alumina (acid or basic) made in Section 13.4.2.

      - If using acid alumina, elute the CDDs/CDFs from the column with 20 mL methylene chloride:hexane (20:80 v/v). Collect the   eluate.

      - If using basic alumina, elute the CDDs/CDFs from the column with 20 mL methylene chloride:hexane (50:50 v/v). Collect the   eluate.

13.4.8   Concentrate the eluate per Sections

  - and 12.7 for further cleanup or injection into the HPLC or GC/MS.

  - Carbon Column.

    - Cut both ends from a 10 mL dispos- able serological pipet (Section 6.7.3.2) to produce a 10 cm column. Fire-polish both ends and flare both ends if desired. Insert a glass-wool plug at one end, and pack the col- umn with 0.55 g of Carbopak/Celite (Section 7.5.3.3) to form an adsorbent bed approxi- mately 2 cm long. Insert a glass-wool plug on top of the bed to hold the adsorbent in place.

    - Pre-elute the column with 5 mL of toluene followed by 2 mL of methylene chlo- ride: methanol:toluene (15:4:1 v/v), 1 mL of methylene chloride:cyclohexane (1:1 v/v), and 5 mL of hexane. If the flow rate of eluate ex- ceeds 0.5 mL/minute, discard the column.

    - When the solvent is within 1 mm of the column packing, apply the sample ex- tract to the column. Rinse the sample con- tainer twice with 1 mL portions of  hexane and apply separately to the column. Apply 2 mL of hexane to complete the transfer.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1613

    - Elute the interfering  compounds with two 3  mL portions  of hexane,  2 mL  of methylene chloride:cyclohexane (1:1 v/v), and

2	mL	of	methylene	chlo- ride:methanol:toluene (15:4:1 v/v). Discard the  eluate.

    - Invert the column, and elute the CDDs/CDFs with 20 mL of toluene. If carbon particles are present in the eluate, filter through glass-fiber filter paper.

    - Concentrate the eluate per Sections

12.6 and 12.7 for further cleanup or injection into the HPLC or GC/MS.

  - HPLC (Reference 6).

    - Column calibration.

      - Prepare a calibration standard containing the  2,3,7,8-substituted  isomers and/or other isomers of interest at a con- centration of approximately 500 pg/L in methylene  chloride.

      - Inject 30 L of the calibration so-

lution into the HPLC and record the signal from the detector. Collect the eluant for reuse. The elution order will be the tetra- through octa-isomers.

      - Establish the collection  time  for the tetra-isomers and for  the  other  isomers of interest. Following calibration, flush the injection system with copious quantities of methylene chloride, including a minimum of five 50 L injections while the detector is monitored, to ensure that residual  CDDs/ CDFs are removed from the system.

      - Verify the calibration with the calibration solution after every 20 extracts. Calibration is verified if the recovery of the CDDs/CDFs from the calibration standard (Section 13.6.1.1) is 75–125% compared to the calibration (Section 13.6.1.2). If calibration is not verified, the system shall be recalibrated using the calibration solution, and the  pre- vious 20 samples shall be re-extracted and cleaned  up  using  the  calibrated  system.

    - Extract  cleanup—HPLC   requires that the column not be overloaded. The col- umn specified in this method is designed to handle a maximum of 30 L of extract. If the extract cannot be concentrated to  less  than 30 L, it is split into fractions and the frac- tions are combined after elution from the column.

      - Rinse the sides  of  the  vial  twice with 30 L of  methylene  chloride  and  reduce to 30 L with the evaporation apparatus (Section 12.7).

      - Inject  the  30  L  extract  into  the

HPLC.

      - Elute the extract using the cali- bration data determined in Section 13.6.1. Collect the fraction(s) in a clean 20 mL con- centrator tube containing 5 mL of hexane:acetone (1:1 v/v).

      - If an extract containing greater than 100 ng/mL of total CDD or  CDF is en- countered, a 30 L methylene chloride blank shall be run through the system to check for carry-over.

      - Concentrate the eluate per Sec- tion 12.7 for injection into the GC/MS.

  - Cleanup of Tissue Lipids—Lipids are removed from the Soxhlet extract using ei- ther the anthropogenic isolation column (Section 13.7.1) or acidified silica gel (Section 13.7.2), or are removed from the HCl digested extract using sulfuric acid and base back-ex- traction (Section 13.7.3).

    - Anthropogenic isolation column (References 22 and 27)—Used for removal of lipids from the Soxhlet/SDS extraction (Sec- tion 12.4.1).

      - Prepare the column as given in Section 7.5.4.

      - Pre-elute the column with 100 mL of hexane. Drain the hexane layer to the top of the column, but do not expose the sodium sulfate.

      - Load the sample and rinses (Sec- tion 12.4.1.9.2) onto the column by draining each portion to the top of the bed. Elute the CDDs/CDFs from the column into the appa- ratus used for concentration (Section 12.4.1.7) using 200 mL of hexane.

      - Concentrate  the  cleaned  up  ex- tract (Sections 12.6 through 12.7) to constant weight per Section 12.7.3.1. If more  than  500 mg of material remains, repeat the cleanup using a fresh anthropogenic isolation  col- umn.

      - Redissolve the extract in a solvent suitable for the additional cleanups to be used (Sections 13.2 through 13.6 and 13.8).

      - Spike 1.0 mL of the cleanup stand- ard (Section 7.11) into the residue/solvent.

      - Clean up the extract using the pro- cedures in Sections 13.2 through 13.6 and 13.8. Alumina (Section 13.4) or Florisil (Section 13.8) and carbon (Section 13.5) are rec- ommended as minimum additional cleanup steps.

      - Following  cleanup,  concentrate the extract to 10 L as described in Section

12.7 and proceed with the analysis in Section 14.

    - Acidified silica gel (Reference 28)— Procedure alternate to the anthropogenic isolation column (Section 13.7.1) that is used for removal of lipids from the Soxhlet/SDS extraction (Section 12.4.1).

      - Adjust  the  volume  of  hexane  in the bottle (Section 12.4.1.9.2) to approxi- mately 200 mL.

      - Spike 1.0 mL of the cleanup stand- ard (Section 7.11) into the residue/solvent.

      - Drop the stirring bar into the bot- tle, place the bottle on the stirring plate, and begin stirring.

      - Add 30–100 g of acid silica gel (Sec- tion 7.5.1.2) to the bottle while stirring, keeping the silica gel in motion. Stir for two to three hours.

NOTE: 30 grams of silica gel should be ade- quate for most samples and will minimize contamination from this source.

#### Pt. 136, App. A, Meth. 1613

      - After stirring, pour the extract through approximately 10 g of granular an- hydrous sodium sulfate (Section 7.2.1) con- tained in  a  funnel  with  glass-fiber  filter  into a  macro  contration  device  (Section  12.6). Rinse the bottle and sodium sulfate with hexane  to  complete  the  transfer.

      - Concentrate the extract per Sec- tions 12.6 through 12.7 and clean up the ex- tract using the procedures in Sections 13.2 through 13.6 and 13.8. Alumina (Section 13.4) or Florisil (Section 13.8) and carbon (Section 13.5) are recommended as minimum addi- tional cleanup steps.

    - Sulfuric acid and base back-extrac- tion. Used with HCl digested extracts (Sec- tion 12.4.2).

      - Spike 1.0 mL of the cleanup stand- ard (Section 7.11) into the residue/solvent (Section 12.4.2.8.2).

      - Add 10 mL of concentrated sul- furic acid to the bottle. Immediately cap and shake one to three times. Loosen cap in a hood to vent excess pressure. Cap and shake the bottle so that the residue/solvent is ex- posed to the acid for a total time of approxi- mately 45 seconds.

      - Decant the hexane into a 250 mL separatory funnel making  sure  that  no  acid is transferred. Complete the quantitative transfer with several hexane rinses.

      - Back extract the solvent/residue with 50 mL of potassium hydroxide solution per Section 12.5.2, followed by two reagent water rinses.

      - Drain the extract through a filter funnel containing approximately 10 g of granular anhydrous sodium sulfate in a glass-fiber filter  into  a macro  concentration device (Section 12.6).

      - Concentrate the cleaned up ex- tract to a volume suitable for the additional cleanups given in Sections 13.2 through 13.6 and 13.8. Gel permeation chromatography (Section 13.2), alumina (Section 13.4) or Florisil (Section 13.8), and Carbopak/Celite (Section 13.5) are recommended as minimum additional cleanup steps.

      - Following  cleanup,  concentrate the  extract  to  10  L  as  described  in  Section

12.7 and proceed with analysis per Section 14.

  - Florisil Cleanup (Reference 29).

    - Pre-elute the activated Florisil col- umn (Section 7.5.3) with 10 mL of methylene chloride followed by 10 mL of hexane:methylene chloride (98:2 v/v) and dis- card  the  solvents.

    - When the solvent is within 1 mm of the packing, apply  the sample  extract (in hexane) to the column. Rinse the sample container twice with 1 mL portions of hexane and apply to the column.

    - Elute  the  interfering   compounds with 20 mL of hexane:methylene chloride (98:2) and discard the eluate.

    - Elute the CDDs/CDFs with 35 mL of methylene  chloride   and  collect   the   eluate.

#### 40 CFR Ch. I (7–1–17 Edition)

Concentrate the eluate per Sections 12.6 through 12.7 for further cleanup or for injec- tion into the HPLC or GC/MS.

14.0    HRGC/HRMS Analysis

  - Establish the operating conditions given in Section 10.1.

  - Add 10 uL of the appropriate internal standard solution (Section 7.12) to the  sam- ple extract immediately prior to injection to minimize the possibility of loss by evapo- ration, adsorption, or  reaction.  If  an  extract is to be reanalyzed and evaporation has oc- curred, do not add more instrument internal standard solution. Rather, bring  the  extract back to its previous volume (e.g., 19 L) with pure nonane only (18 L if 2 L injections are used).

  - Inject 1.0 L or 2.0 L of the con- centrated extract containing the internal standard solution, using on-column  or splitless injection. The volume injected must be identical to the volume used for calibra- tion (Section 10). Start the GC  column  ini- tial  isothermal  hold  upon  injection.  Start MS data collection after the solvent peak elutes. Stop data collection after the OCDD and OCDF have eluted. If only 2,3,7,8-TCDD and 2,3,7,8-TCDF are to be determined, stop data collection after elution of these com- pounds. Return the column to the initial temperature for analysis of  the  next  extract or standard.

15.0   System and Laboratory Performance

  - At the beginning of each 12-hour shift during which analyses are performed, GC/MS system performance and calibration are verified for all CDDs/CDFs and labeled com- pounds. For these tests, analysis of the CS3 calibration verification (VER) standard (Sec- tion 7.13 and Table 4) and the isomer speci- ficity test standards (Section 7.15 and Table

5) shall be used to verify all performance cri- teria. Adjustment and/or recalibration (Sec- tion 10) shall be performed until all perform- ance criteria are met. Only after all perform- ance criteria are met may samples, blanks, IPRs, and OPRs be analyzed.

  - MS Resolution—A static  resolving power of at least 10,000 (10% valley defini- tion) must be demonstrated at  the  appro- priate m/z before any analysis is performed. Static resolving power checks must be per- formed at the beginning and at the end of each 12-hour shift according to procedures in Section 10.1.2. Corrective actions must be implemented whenever the resolving power does  not  meet  the  requirement.

  - Calibration Verification.

    - Inject the VER standard using the procedure in Section 14.

    - The m/z abundance ratios for all CDDs/CDFs shall be within the  limits  in Table  9;  otherwise,  the  mass  spectrometer

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1613

shall be adjusted until the m/z abundance ra- tios fall within the limits specified, and the verification test shall be repeated. If the ad- justment alters the resolution of the mass spectrometer, resolution shall be verified (Section 10.1.2) prior to repeat of the verification   test.

    - The peaks representing each CDD/ CDF and labeled compound in the VER standard must be present with S/N of at least 10; otherwise, the mass spectrometer shall be adjusted and the verification test repeated.

    - Compute the concentration of each CDD/CDF compound by isotope dilution (Section 10.5) for those compounds that have labeled analogs (Table 1). Compute the con- centration of the labeled compounds by the internal standard method (Section 10.6). These concentrations are computed based on the calibration data in Section 10.

    - For each compound, compare the concentration  with  the  calibration verification limit in Table 6. If only 2,3,7,8- TCDD and 2,3,7,8-TCDF are to be determined, compare the concentration to the limit in Table 6a. If all compounds meet the accept- ance criteria, calibration has been verified and analysis of standards and sample ex- tracts may proceed. If, however, any com- pound fails its respective limit, the measure- ment system is not performing properly for that compound. In this event, prepare a fresh calibration standard or correct the problem causing the failure and repeat the resolution (Section 15.2) and verification (Section 15.3) tests, or recalibrate (Section 10).

  - Retention Times and GC Resolution.

    - Retention times.

      - Absolute—The absolute retention times of the 13C12-1,2,3,4–TCDD and 13C12- 1,2,3,7,8,9-HxCDD   GCMS   internal   standards in the verification test (Section 15.3) shall be within 15 seconds of the retention times ob- tained during calibration (Sections 10.2.1 and 10.2.4).

      - Relative—The relative retention times of CDDs/CDFs and labeled compounds in the verification test (Section 15.3) shall be within the limits given in Table 2.

    - GC resolution.

      - Inject the isomer specificity standards (Section 7.15) on their respective columns.

      - The valley height between 2,3,7,8- TCDD and the other tetra-dioxin isomers at m/z 319.8965, and between 2,3,7,8-TCDF and the other tetra-furan isomers at m/z 303.9016 shall not exceed 25% on their respective col- umns (Figures 6 and 7).

    - If the  absolute  retention  time  of any compound is not within the limits speci- fied or if the 2,3,7,8-isomers are not resolved, the GC is not performing properly. In this event, adjust the GC and repeat the verification test (Section 15.3) or recalibrate (Section 10), or replace the GC column and either verify calibration or recalibrate.

  - Ongoing Precision and Recovery.

    - Analyze the extract of the ongoing precision and recovery (OPR) aliquot (Sec- tion 11.4.2.5, 11.5.4, 11.6.2, 11.7.4, or 11.8.3.2) prior to analysis of samples from the same batch.

    - Compute the concentration of each CDD/CDF by isotope dilution for those com- pounds that have labeled analogs (Section 10.5). Compute the concentration of 1,2,3,7,8,9-HxCDD, OCDF, and each labeled compound by the internal standard method (Section 10.6).

    - For each CDD/CDF and labeled com- pound, compare the  concentration  to  the OPR limits given in Table 6. If only 2,3,7,8- TCDD and 2,3,7,8-TCDF are to be determined, compare the concentration to the limits in Table 6a. If all compounds meet the accept- ance criteria, system performance is accept- able and analysis of blanks and samples may proceed. If, however, any individual con- centration falls outside of the range  given, the extraction/concentration processes  are not being performed properly for that com- pound. In this event, correct the problem, re- prepare, extract, and clean up the sample batch and repeat the ongoing precision and recovery test (Section 15.5).

    - Add results that pass the specifica- tions in Section 15.5.3 to initial and previous ongoing data for each compound in each ma- trix. Update QC charts to form a graphic rep- resentation of continued laboratory perform- ance. Develop a statement of laboratory ac- curacy for each  CDD/CDF  in  each  matrix type by calculating the average percent re- covery (R) and the standard deviation of per- cent recovery (SR). Express the accuracy as a recovery interval from R¥2SR to R  =  2SR. For example, if R = 95% and SR = 5%, the ac- curacy is 85–105%.

15.6 Blank—Analyze the method blank ex- tracted with each sample batch immediately following analysis of the OPR aliquot to demonstrate freedom from contamination and freedom from carryover from the OPR analysis. The results of the analysis of the blank must meet the specifications in Sec- tion 9.5.2 before sample analyses may pro- ceed.

16.0    Qualitative Determination

A CDD, CDF, or labeled compound is iden- tified in a standard, blank,  or  sample  when all  of  the  criteria  in  Sections  16.1  through

16.4 are met.

  - The signals for the two exact m/z’s in Table 8 must be present and must maximize within the same two seconds.

  - The signal-to-noise ratio (S/N) for the GC peak at each exact m/z must be greater than or equal to 2.5 for each CDD or CDF de- tected in a sample extract, and greater than or equal to 10 for all CDDs/CDFs in the cali- bration standard (Sections 10.2.3 and 15.3.3).

#### Pt. 136, App. A, Meth. 1613

  - The ratio of the integrated areas  of the two exact m/z’s specified in Table 8 must be within the limit in Table 9, or within 10% of the ratio in the midpoint (CS3) calibration or calibration verification  (VER),  whichever is most recent.

  - The relative retention time  of  the peak for a 2,3,7,8-substituted CDD or CDF must be within the limit in Table 2. The re- tention time of peaks representing non- 2,3,7,8-substituted CDDs/CDFs must be with- in the retention time windows established in Section 10.3.

  - Confirmatory Analysis—Isomer speci- ficity for 2,3,7,8-TCDF cannot be achieved on the DB–5 column. Therefore, any sample in which 2,3,7,8-TCDF is identified by  analysis on a DB–5 column must have a confirmatory analysis performed on a DB–225, SP–2330, or equivalent GC column. The operating condi- tions in Section 10.1.1 may be adjusted to op- timize the analysis on the second GC col- umn, but the GC/MS must meet the mass resolution and calibration specifications in Section 10.

  - If the criteria for identification in Sections 16.1 through 16.5 are not met, the CDD or CDF has not been identified and the results may not be reported for regulatory compliance purposes. If interferences pre- clude identification, a new aliquot of sample must be extracted, further cleaned up, and analyzed.

  - Quantitative Determination

  - Isotope Dilution Quantitation—By adding a known amount of a labeled com- pound to every sample prior to extraction, correction for recovery of the CDD/CDF can be made because the CDD/CDF and its la- beled analog exhibit similar effects upon ex- traction,   concentration,   and   gas   chroma-

#### 40 CFR Ch. I (7–1–17 Edition)

17.1.1 Because of a potential interference, the labeled analog of OCDF is not added to the sample. Therefore, OCDF is quantitated against labeled OCDD. As a result, the con- centration of OCDF is corrected for the re- covery of the labeled OCDD. In instances where OCDD and OCDF behave differently during sample extraction, concentration, and cleanup procedures, this may decrease the accuracy of the OCDF results. However, given the low toxicity of this compound rel- ative to the other dioxins and furans, the po- tential decrease in accuracy is not consid- ered significant.

17.1.2 Because 13C12-1,2,3,7,8,9-HxCDD is used as an instrument internal standard (i.e., not added before extraction of the sample), it cannot be  used to  quantitate the  1,2,3,7,8,9- HxCDD by strict isotope dilution procedures. Therefore, 1,2,3,7,8,9-HxCDD is quantitated using the averaged response of the labeled analogs of the other two 2,3,7,8-substituted HxCDD’s: 1,2,3,4,7,8-HxCDD and 1,2,3,6,7,8- HxCDD. As a result, the concentration of 1,2,3,7,8,9-HxCDD is corrected for the average recovery of the other two HxCDD’s.

17.1.3 Any peaks representing non-2,3,7,8- substituted  CDDs/CDFs  are  quantitated using an average of the response factors from all of the labeled 2,3,7,8-isomers at the same level  of  chlorination.

17.2 Internal Standard  Quantitation and Labeled Compound Recovery.

17.2.1 Compute the concentrations of 1,2,3,7,8,9-HxCDD, OCDF,  the  13C-labeled analogs and the 37C-labeled cleanup standard in the extract using the response factors de- termined from the initial calibration data (Section 10.6) and the following equation:

A1s A2s Cis

tography. Relative response (RR) values are used in conjunction with the initial calibra-

Cex

## (ng/mL) 

A1

## A2

RF

tion data described in Section 10.5 to deter- mine concentrations directly, so long as la-

where:

is	is

beled compound spiking levels are constant, using the following equation:

A1n A2n Cl

Cex = The concentration of the CDD/CDF in the extract, and the other terms are as defined in Section 10.6.1.

NOTE: There is only one m/z for the 37Cl-la-

Cex

## (ng/mL) 

A1

- A2 RR

beled standard.

where:

l	l	17.2.2   Using   the   concentration   in   the   ex-

tract determined above, compute the percent

Cex = The concentration of the CDD/CDF in the extract, and the other terms are as defined in Section 10.5.2.

recovery of the 13C-labeled compounds and the 37C-labeled cleanup standard using the following equation:

## Recovery (%) = Concentration found (g/mL) 100

Concentration spiked (g/mL)

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1613

  - The concentration of a CDD/CDF in the solid phase of the sample is computed using the concentration of the compound in

the extract and the weight of the solids (Sec- tion 11.5.1), as follows:

## Concentration in solid (ng/kg) =

Cex Vex 

Ws

where:

Cex = The concentration of the compound in the extract.

Vex = The extract volume in mL.

Ws  = The sample weight (dry weight) in kg.

  - The concentration of a CDD/CDF in the aqueous phase of the sample is computed using the concentration of the compound  in the extract and the volume of water  ex- tracted (Section 11.4 or 11.5), as follows:

## Concentration in aqueous phase(pg/L) =

Cex Vex 

Vs

where:

Cex = The concentration of the compound in the extract.

Vex = The extract volume in mL. Vs = The sample volume in liters.

  - If the SICP area at either quantita- tion m/z for any compound exceeds the cali- bration range of the system, a smaller sam- ple aliquot is extracted.

    - For aqueous samples containing 1% solids or less, dilute 100 mL, 10 mL, etc., of sample to 1 L with reagent water and re-pre- pare, extract, clean up, and analyze per Sec- tions 11 through 14.

    - For  samples  containing   greater than 1% solids, extract an amount of sample equal to 1⁄10, 1⁄100, etc., of the amount used in Section 11.5.1. Re-prepare, extract, clean up, and analyze per Sections 11 through 14.

    - If a smaller sample size will not be representative of the entire sample, dilute the sample extract by a factor  of  10,  adjust the concentration of the instrument internal standard to 100 pg/L in the extract, and ana- lyze an aliquot of this diluted extract by the internal standard method.

  - Results are reported to three signifi- cant figures for the CDDs/CDFs and labeled compounds found in all standards, blanks, and samples.

    - Reporting units and levels.

      - Aqueous samples—Report results in pg/L (parts-per-quadrillion).

      - Samples containing greater than 1% solids (soils, sediments, filter cake, com- post)—Report results in ng/kg based on the dry weight of the sample. Report the percent solids so that the result may be corrected.

      - Tissues—Report results in ng/kg of wet tissue, not on the basis of the lipid con- tent of the sample. Report the percent lipid content, so that the data user can calculate the concentration on a lipid basis if desired.

      - Reporting level.

        - Standards (VER, IPR, OPR) and samples—Report results at or above the min- imum level (Table 2). Report results below the minimum level as not detected or as re- quired by the regulatory authority.

        - Blanks—Report results above one-third the ML.

    - Results for CDDs/CDFs in samples that have been diluted are reported at the least dilute level at which the areas at the quantitation m/z’s are within the calibration range (Section 17.5).

    - For CDDs/CDFs having a labeled analog, results are reported at the least di- lute level at which the area at the quantita- tion m/z is within the calibration range (Sec- tion 17.5) and the labeled compound recovery is within the normal range for the method (Section 9.3 and Tables 6, 6a, 7, and 7a).

    - Additionally, if requested, the total concentration of all isomers in an individual level of chlorination (i.e., total TCDD, total TCDF, total Paced, etc.) may be reported by summing the concentrations of all isomers identified in that level of chlorination, in- cluding both 2,3,7,8-substituted and non- 2,3,7,8-substituted isomers.

18.0    Analysis of Complex Samples

  - Some samples may contain high lev- els (>10 ng/L; >1000 ng/kg) of the compounds of interest, interfering compounds, and/or polymeric  materials.  Some  extracts  will  not

#### Pt. 136, App. A, Meth. 1613

concentrate to 10 L (Section 12.7); others may overload the GC column and/or mass spectrometer.

  - Analyze a smaller aliquot of the sam- ple (Section 17.5) when the extract will not concentrate to 10 L after all cleanup proce- dures have been exhausted.

  - Chlorodiphenyl	Ethers—If chromatographic peaks are detected at the retention time of any CDDs/CDFs in any of the m/z channels being monitored for the chlorodiphenyl ethers (Table 8), cleanup pro- cedures must be employed until these inter- ferences are removed. Alumina (Section 13.4) and Florisil (Section 13.8) are recommended for removal of chlorodiphenyl ethers.

  - Recovery of Labeled Compounds—In most samples, recoveries of the labeled com- pounds will be similar to those from reagent water or from the alternate matrix (Section 7.6).

    - If the recovery of any of the labeled compounds is outside of the normal range (Table 7), a diluted sample shall be analyzed (Section 17.5).

    - If the recovery of any of the labeled compounds in the diluted  sample  is  outside of normal range, the calibration verification standard (Section 7.13) shall be analyzed and calibration verified (Section 15.3).

    - If the calibration cannot be verified, a new calibration must be performed and the original sample extract reanalyzed.

    - If the calibration is verified and the diluted sample does not meet the limits for labeled compound recovery, the method does not apply to the sample being analyzed and the result may not be reported for regu- latory compliance purposes. In this case, al- ternate extraction and cleanup procedures in this method must be employed to resolve the interference. If all cleanup procedures in this method have been employed and labeled compound recovery remains outside of the normal range, extraction and/or cleanup pro- cedures that are beyond this scope of this method will be required to analyze these samples.

19.0    Pollution Prevention

  - The solvents used in this method pose little threat to the environment when man- aged properly. The solvent evaporation tech- niques used in this method are amenable to solvent recovery, and it is recommended that the laboratory recover solvents wherever feasible.

  - Standards should be prepared in vol- umes consistent with laboratory use to mini- mize disposal of standards.

20.0    Waste Management

  - It is the laboratory’s responsibility to comply with all federal, state, and local reg- ulations governing waste management, par- ticularly the hazardous waste identification

#### 40 CFR Ch. I (7–1–17 Edition)

rules and land disposal restrictions, and to protect the air, water, and land by mini- mizing and controlling all releases  from fume hoods and bench operations. Compli- ance is also required with any sewage dis- charge permits and regulations.

  - Samples containing HCl to pH <2 are hazardous and must be neutralized before being poured down a drain or must be han- dled as hazardous waste.

  - The  CDDs/CDFs  decompose  above  800

C. Low-level waste such as absorbent paper, tissues, animal remains, and plastic gloves may be burned in an appropriate incinerator. Gross quantities (milligrams) should be packaged securely and disposed of through commercial or governmental channels that are capable of handling extremely toxic wastes.

  - Liquid or soluble waste should be dis- solved in methanol or ethanol and irradiated with ultraviolet light with a wavelength shorter than 290 nm for several days. Use F40 BL or equivalent lamps. Analyze  liquid wastes, and dispose of the solutions when the CDDs/CDFs can no longer be detected.

  - For further information on waste management, consult  ‘‘The Waste  Manage- ment Manual for Laboratory Personnel’’ and ‘‘Less is Better—Laboratory Chemical Man- agement  for  Waste  Reduction,’’  available from the American Chemical Society’s De- partment of Government  Relations  and Science Policy, 1155 16th Street N.W., Wash- ington, D.C. 20036.

21.0   Method Performance

Method performance was validated and performance specifications were developed using data from EPA’s international inter- laboratory  validation  study  (References  30–

- and the EPA/paper industry Long-Term Variability Study of discharges  from  the pulp and paper industry (58 FR 66078).

22.0   References

  - Tondeur, Yves. ‘‘Method 8290: Analytical Procedures and Quality Assurance for Multi- media Analysis of Polychlorinated Dibenzo- p-dioxins and Dibenzofurans by High Resolu- tion Gas Chromatography/High Resolution Mass Spectrometry,’’ USEPA EMSL,  Las Vegas, Nevada, June 1987.

  - ‘‘Measurement	of	2,3,7,8- Tetrachlorinated Dibenzo-p-dioxin (TCDD) and 2,3,7,8-Tetrachlorinated Dibenzofuran (TCDF) in  Pulp,  Sludges,  Process  Samples and Wastewaters from  Pulp  and  Paper Mills,’’ Wright State University, Dayton, OH 45435, June 1988.

  - ‘‘NCASI Procedures for the Preparation and Isomer Specific Analysis of  Pulp  and Paper Industry Samples for 2,3,7,8-TCDD and 2,3,7,8-TCDF,’’ National Council of the Paper Industry for Air and Stream Improvement Inc.,   260   Madison   Avenue,   New   York,   NY

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1613

10016, Technical Bulletin No. 551, Pre-Release

Copy, July 1988.

  - ‘‘Analytical Procedures and Quality As- surance Plan for the Determination of PCDD/PCDF  in  Fish,’’  USEPA,  Environ- mental Research Laboratory, 6201 Congdon Boulevard, Duluth, MN 55804, April 1988.

  - Tondeur, Yves. ‘‘Proposed GC/MS Meth- odology  for  the  Analysis  of  PCDDs  and PCDFs in Special Analytical Services Sam- ples,’’ Triangle Laboratories, Inc., 801–10 Capitola Dr, Research Triangle  Park,  NC 27713, January 1988; updated by personal communication  September  1988.

  - Lamparski,   L.L.  and   Nestrick,   T.J.  ‘‘De- termination    of    Tetra-,    Hexa-,    Hepta-,    and Octachlorodibenzo-p-dioxin    Isomers    in    Par- ticulate   Samples   at   Parts   per   Trillion   Lev- els,’’    Analytical    Chemistry,    52:    2045–2054, 1980.

  - Lamparski, L.L. and Nestrick, T.J. ‘‘Novel Extraction Device for the Determina- tion of Chlorinated Dibenzo-p-dioxins (PCDDs) and Dibenzofurans (PCDFs) in Mat- rices Containing Water,’’ Chemosphere, 19:27–31,  1989.

  - Patterson, D.G., et. al. ‘‘Control of Inter- ferences in the Analysis of Human Adipose Tissue for 2,3,7,8-Tetrachlorodibenzo-p- dioxin,’’ Environmental Toxicological Chem- istry, 5:355–360, 1986.

  - Stanley, John S. and Sack, Thomas M. ‘‘Protocol for the Analysis of 2,3,7,8- Tetrachlorodibenzo-p-dioxin by High Resolu- tion Gas Chromatography/High Resolution Mass Spectrometry,’’ USEPA EMSL, Las Vegas, Nevada 89114, EPA 600/4–86–004, Janu- ary 1986.

  - ‘‘Working with Carcinogens,’’ Depart- ment of Health, Education, & Welfare, Public Health Service, Centers for Disease Control, NIOSH,  Publication  77–206,  August  1977, NTIS PB–277256.

  - ‘‘OSHA Safety and Health Standards, General Industry,’’ OSHA 2206, 29 CFR 1910.

  - ‘‘Safety in Academic Chemistry Labora- tories,’’ ACS Committee on Chemical Safety, 1979.

  - ‘‘Standard Methods for the  Examina- tion of Water and Wastewater,’’ 18th edition and later revisions, American Public Health Association, 1015 15th St, N.W., Washington, DC 20005, 1–35: Section 1090 (Safety), 1992.

14.	‘‘Method	613—2,3,7,8-

Tetrachlorodibenzo-p-dioxin,’’   40   CFR   136   (49

FR 43234), October 26, 1984, Section 4.1.

- Provost,  L.P.  and  Elder,  R.S.  ‘‘Inter- pretation of Percent Recovery Data,’’ Amer- ican Laboratory, 15: 56–83, 1983.

- ‘‘Standard Practice for Sampling Water,’’ ASTM Annual Book of Standards, ASTM, 1916 Race Street, Philadelphia, PA 19103–1187, 1980.

- ‘‘Methods 330.4 and 330.5 for Total Re- sidual Chlorine,’’ USEPA, EMSL, Cincinnati, OH 45268, EPA 600/4–79–020, March 1979.

- ‘‘Handbook of Analytical Quality Con- trol in Water and Wastewater Laboratories,’’ USEPA EMSL, Cincinnati, OH 45268, EPA– 600/4–79–019, March 1979.

- Williams, Rick. Letter  to  Bill  Telliard, June 4, 1993, available from the EPA Sample Control Center operated  by  DynCorp  Viar, Inc., 300 N Lee St, Alexandria, VA 22314, 703– 519–1140.

- Barkowski, Sarah. Fax to Sue Price, August 6, 1992, available from the EPA Sam- ple Control Center operated  by  DynCorp Viar, Inc., 300 N Lee St, Alexandria VA 22314, 703–519–1140.

- ‘‘Analysis of  Multi-media,  Multi-con- centration Samples for Dioxins and Furans, PCDD/PCDF Analyses Data Package’’, Nar- rative for Episode 4419, MRI Project No. 3091- A, op.cit. February 12, 1993, Available  from the EPA Sample  Control Center operated  by DynCorp Viar Inc, 300 N  Lee  St,  Alexandria, VA 22314 (703–519–1140).

- ‘‘Analytical Procedures and Quality As- surance Plan for the Determination of PCDD/PCDF in Fish’’, U.S. Environmental Protection Agency, Environmental Research Laboratory, Duluth, MN 55804, EPA/600/3–90/ 022, March 1990.

- Afghan, B.K., Carron, J., Goulden, P.D., Lawrence, J., Leger, D., Onuska, F., Sherry, J., and Wilkenson, R.J., ‘‘Recent Advances in Ultratrace Analysis of Dioxins and Related Halogenated Hydrocarbons’’, Can J. Chem., 65: 1086–1097, 1987.

- Sherry, J.P. and Tse, H.  ‘‘A  Procedure for the Determination of Polychlorinated Dibenzo-p-dioxins in Fish’’, Chemosphere, 20: 865–872, 1990.

- ‘‘Preliminary Fish Tissue Study’’, Re- sults of Episode 4419, available from the EPA Sample Control Center operated by DynCorp Viar, Inc., 300 N  Lee  St,  Alexandria,  VA 22314, 703–519–1140.

- Nestrick, Terry L. DOW Chemical Co., personal communication with D.R. Rushneck, April 8, 1993. Details available from the U.S. Environmental Protection Agency Sample Control Center operated by DynCorp Viar Inc, 300 N Lee St, Alexandria, VA 22314, 703–519–1140.

- Barnstadt, Michael. ‘‘Big Fish  Col- umn’’, Triangle  Laboratories  of  RTP,  Inc., SOP 129–90, 27 March 27, 1992.

- ‘‘Determination of Polychlorinated Dibenzo-p-Dioxins (PCDD) and Dibenzofurans (PCDF)   in   Environmental   Samples    Using EPA Method 1613’’, Chemical Sciences De- partment, Midwest Research Institute, 425 Volker Boulevard, Kansas City, MO 44110– 2299, Standard Operating Procedure No. CS– 153, January 15, 1992.

- Ryan, John J. Raymonde Lizotte and William H. Newsome, J. Chromatog. 303 (1984) 351-360.

- Telliard, William A., McCarty, Harry B., and Riddick, Lynn S. ‘‘Results of the Interlaboratory Validation Study of USEPA

#### Pt. 136, App. A, Meth. 1613

Method 1613 for the  Analysis  of  Tetra- through  Octachlorinated  Dioxins  and  Furans by  Isotope  Dilution  GC/MS,’’  Chemosphere, 27, 41–46 (1993).

- ‘‘Results of the International Interlab- oratory Validation Study of USEPA Method

#### 40 CFR Ch. I (7–1–17 Edition)

1613’’, October 1994, available from the EPA Sample Control Center operated by DynCorp Viar, Inc., 300 N  Lee  St,  Alexandria,  VA 22314, 703–519–1140.

23.0  Tables and Figures

TABLE 1—CHLORINATED DIBENZO-P-DIOXINS AND FURANS DETERMINED BY ISOTOPE DILUTION AND INTERNAL  STANDARD  HIGH  RESOLUTION  GAS  CHROMATOGRAPHY  (HRGC)/HIGH  RESOLUTION MASS SPECTROMETRY (HRMS)

| CDDs/CDFs 1 | CAS registry | Labeled analog | CAS registry |
| --- | --- | --- | --- |
| 2,3,7,8-TCDD ................................................... | 1746–01–6 | 13C12-2,3,7,8-TCDD ........................................ | 76523–40–5 |
|  |  | 37Cl4-2,3,7,8-TCDD ......................................... | 85508–50–5 |
| Total TCDD ...................................................... | 41903–57–5 |  |  |
| 2,3,7,8-TCDF ................................................... | 51207–31–9 | 13C12-2,3,7,8-TCDF ......................................... | 89059–46–1 |
| Total-TCDF ...................................................... | 55722–27–5 |  |  |
| 1,2,3,7,8-PeCDD ............................................. | 40321–76–4 | 13C12-1,2,3,7,8-PeCDD ................................... | 109719–79–1 |
| Total-PeCDD ................................................... | 36088–22–9 |  |  |
| 1,2,3,7,8-PeCDF .............................................. | 57117–41–6 | 13C12-1,2,3,7,8-PeCDF .................................... | 109719–77–9 |
| 2,3,4,7,8-PeCDF .............................................. | 57117–31–4 | 13C12-2,3,4,7,8-PeCDF .................................... | 116843–02–8 |
| Total-PeCDF .................................................... | 30402–15–4 |  |  |
| 1,2,3,4,7,8-HxCDD .......................................... | 39227–28–6 | 13C12-1,2,3,4,7,8-HxCDD ................................ | 109719–80–4 |
| 1,2,3,6,7,8-HxCDD .......................................... | 57653–85–7 | 13C12-1,2,3,6,7,8-HxCDD ................................ | 109719–81–5 |
| 1,2,3,7,8,9-HxCDD .......................................... | 19408–74–3 | 13C12-1,2,3,7,8,9-HxCDD ................................ | 109719–82–6 |
| Total-HxCDD ................................................... | 34465–46–8 |  |  |
| 1,2,3,4,7,8-HxCDF ........................................... | 70648–26–9 | 13C12-1,2,3,4,7,8-HxCDF ................................. | 114423–98–2 |
| 1,2,3,6,7,8-HxCDF ........................................... | 57117–44–9 | 13C12-1,2,3,6,7,8-HxCDF ................................. | 116843–03–9 |
| 1,2,3,7,8,9-HxCDF ........................................... | 72918–21–9 | 13C12-1,2,3,7,8,9-HxCDF ................................. | 116843–04–0 |
| 2,3,4,6,7,8-HxCDF ........................................... | 60851–34–5 | 13C12-2,3,4,6,7,8-HxCDF ................................. | 116843–05–1 |
| Total-HxCDF .................................................... | 55684–94–1 |  |  |
| 1,2,3,4,6,7,8-HpCDD ....................................... | 35822–46–9 | 13C12-1,2,3,4,6,7,8-HpCDD ............................. | 109719–83–7 |
| Total-HpCDD ................................................... | 37871–00–4 |  |  |
| 1,2,3,4,6,7,8-HpCDF ........................................ | 67562–39–4 | 13C12-1,2,3,4,6,7,8-HpCDF ............................. | 109719–84–8 |
| 1,2,3,4,7,8,9-HpCDF ........................................ | 55673–89–7 | 13C12-1,2,3,4,7,8,9-HpCDF ............................. | 109719–94–0 |
| Total-HpCDF .................................................... | 38998–75–3 |  |  |
| OCDD .............................................................. | 3268–87–9 | 13C12-OCDD .................................................... | 114423–97–1 |
| OCDF ............................................................... | 39001–02–0 | Not used. |  |

1 Chlorinated dibenzo-p-dioxins and chlorinated dibenzofurans. TCDD = Tetrachlorodibenzo-p-dioxin.

TCDF = Tetrachlorodibenzofuran. PeCDD = Pentachlorodibenzo-p-dioxin. PeCDF = Pentachlorodibenzofuran.

HxCDD = Hexachlorodibenzo-p-dioxin. HxCDF = Hexachlorodibenzofuran.

HpCDD = Heptachlorodibenzo-p-dioxin. HpCDF = Heptachlorodibenzofuran.

OCDD = Octachlorodibenzo-p-dioxin. OCDF = Octachlorodibenzofuran.

TABLE 2—RETENTION TIME REFERENCES, QUANTITATION REFERENCES, RELATIVE RETENTION TIMES,

AND MINIMUM LEVELS FOR CDDS AND DCFS

| CDD/CDF | Retention time and quantitation reference | Relative reten- tion time | Minimum level 1 |
| --- | --- | --- | --- |
|  |  |  | Water (pg/L; ppq) | Solid (ng/ kg; ppt) | Extract (pg/L; ppb) |

Compounds using 13 C12–1,2,3,4-TCDD as the Injection Internal Standard

| 2,3,7,8-TCDF ................................... | 13 C12-2,3,7,8-TCDF ........................ | 0.999–1.003 | 10 | 1 | 0.5 |
| --- | --- | --- | --- | --- | --- |
| 2,3,7,8-TCDD ................................... | 13 C12-2,3,7,8-TCDD ........................ | 0.999–1.002 | 10 | 1 | 0.5 |
| 1,2,3,7,8-Pe ..................................... | 13 C12-1,2,3,7,8-PeCDF ................... | 0.999–1.002 | 50 | 5 | 2.5 |
| 2,3,4,7,8-PeCDF .............................. | 13 C12-2,3,4,7,8-PeCDF ................... | 0.999–1.002 | 50 | 5 | 2.5 |
| 1,2,3,7,8-PeCDD ............................. | 13 C12-1,2,3,7,8-PeCDD .................. | 0.999–1.002 | 50 | 5 | 2.5 |
| 13 C12-2,3,7,8-TCDF ......................... | 13 C12-1,2,3,4-TCDD ........................ | 0.923–1.103 |  |  |  |
| 13 C12-2,3,7,8-TCDD ........................ | 13 C12-1,2,3,4-TCDD ........................ | 0.976–1.043 |  |  |  |
| 13 C12-2,3,7,8-TCDD ........................ | 13 C12-1,2,3,4-TCDD ........................ | 0.989–1.052 |  |  |  |
| 13 C12-1,2,3,7,8-PeCDF .................... | 13 C12-1,2,3,4-TCDD ........................ | 1.000–1.425 |  |  |  |
| 13 C12-2,3,4,7,8-PeCDF .................... | 13 C12-1,2,3,4-TCDD ........................ | 1.001–1.526 |  |  |  |
| 13 C12-1,2,3,7,8-PeCDF .................... | 13 C12-1,2,3,4-TCDD ........................ | 1.000–1.567 |  |  |  |

Compounds using 13 C12–1,2,3,7,8,9-HxCDD as the Injection Internal Standard

1,2,3,4,7,8-HxCDF ........................... 13 C12-1,2,3,4,7,8-HxCDF ................	0.999–1.001

50

5

2.5

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1613

TABLE 2—RETENTION TIME REFERENCES, QUANTITATION REFERENCES, RELATIVE RETENTION TIMES,

AND MINIMUM LEVELS FOR CDDS AND DCFS—Continued

| CDD/CDF | Retention time and quantitation reference | Relative reten- tion time | Minimum level 1 |
| --- | --- | --- | --- |
|  |  |  | Water (pg/L; ppq) | Solid (ng/ kg; ppt) | Extract (pg/L; ppb) |
| 1,2,3,6,7,8-HxCDF ........................... | 13 C12-1,2,3,6,7,8-HxCDF ................ | 0.997–1.005 | 50 | 5 | 2.5 |
| 1,2,3,7,8,9-HxCDF ........................... | 13 C12-1,2,3,7,8,9-HxCDF ................ | 0.999–1.001 | 50 | 5 | 2.5 |
| 2,3,4,6,7,8-HxCDF ........................... | 13 C12-2,3,4,6,7,8-HxCDF ................ | 0.999–1.001 | 50 | 5 | 2.5 |
| 1,2,3,4,7,8-HxCDD .......................... | 13 C12-1,2,3,4,7,8-HxCDD ............... | 0.999–1.001 | 50 | 5 | 2.5 |
| 1,2,3,6,7,8-HxCDD .......................... | 13 C12-1,2,3,6,7,8-HxCDD ............... | 0.998–1.004 | 50 | 5 | 2.5 |
| 1,2,3,7,8,9-HxCDD .......................... | (2) .................................................... | 1.000–1.019 | 50 | 5 | 2.5 |
| 1,2,3,4,6,7,8-HpCDF ........................ | 13 C12-1,2,3,4,6,7,8-HpCDF ............. | 0.999–1.001 | 50 | 5 | 2.5 |
| 1,2,3,4,7,8,9-HpCDF ........................ | 13 C12-1,2,3,4,7,8,9-HpCDF ............. | 0.999–1.001 | 50 | 5 | 2.5 |
| 1,2,3,4,6,7,8-HpCDD ....................... | 13 C12-1,2,3,4,6,7,8-HpCDD ............ | 0.999–1.001 | 50 | 5 | 2.5 |
| OCDF ............................................... | 13 C12-OCDD ................................... | 0.999–1.001 | 100 | 10 | 5.0 |
| OCDD .............................................. | 13 C12-OCDD ................................... | 0.999–1.001 | 100 | 10 | 5.0 |
| 1,2,3,4,6,7,8,-HxCDF ....................... | 13 C12-1,2,3,7,8,9-HpCDD ............... | 0.949–0.975 |  |  |  |
| 13 C121,2,3,7,8,9-HxCDF .................. | 13 C12-1,2,3,7,8,9-HpCDD ............... | 0.977–1.047 |  |  |  |
| 13 C122,3,4,6,7,8,-HxCDF ................. | 13 C12-1,2,3,7,8,9-HpCDD ............... | 0.959–1.021 |  |  |  |
| 13 C121,2,3,4,7,8,-HxCDF ................. | 13 C12-1,2,3,7,8,9-HpCDD ............... | 0.977–1.000 |  |  |  |
| 13 C121,2,3,6,7,8,-HxCDF ................. | 13 C12-1,2,3,7,8,9-HpCDD ............... | 0.981–1.003 |  |  |  |
| 13 C121,2,3,4,6,7,8-HxCDF ............... | 13 C12-1,2,3,7,8,9-HpCDD ............... | 1.043–1.085 |  |  |  |
| 13 C121,2,3,4,7,8,9-HxCDF ............... | 13 C12-1,2,3,7,8,9-HpCDD ............... | 1.057–1.151 |  |  |  |
| 13 C121,2,3,4,6,7,8-HxCDF ............... | 13 C12-1,2,3,7,8,9-HpCDD ............... | 1.086–1.110 |  |  |  |
| 13 C12OCDD ..................................... | 13 C12-1,2,3,7,8,9-HpCDD ............... | 1.032–1.311 |  |  |  |

1 The Minimum Level (ML) for each analyte is defined as the level at which the entire analytical system must give a recogniz- able signal and acceptable calibration point. It is equivalent to the concentration of the lowest calibration standard, assuming that all method-specified sample weights, volumes, and cleanup procedures have been employed.

2 The retention time reference for 1,2,3,7,8,9-HxCDD is 13C12-1,2,3,6,7,8-HxCDD, and 1,2,3,7,8,9-HxCDD is quantified using the averaged responses for 13C12-1,2,3,4,7,8-HxCDD and 13C12-1,2,3,6,7,8-HxCDD.

TABLE 3—CONCENTRATION OF STOCK AND SPIKING SOLUTIONS CONTAINING CDDS/CDFS AND

LABELED COMPOUNDS

| CDD/CDF | Labeled com- pound stock solution 1 (ng/mL) | Labeled compound spiking solu- tion 2 (ng/mL) | PAR stock solution 3 (ng/mL) | PAR spiking solution 4 (ng/mL) |
| --- | --- | --- | --- | --- |
| 2,3,7,8-TCDD .................................................................................... | ...................... | .................... | 40 | 0.8 |
| 2,3,7,8-TCDF ..................................................................................... | ...................... | .................... | 40 | 0.8 |
| 1,2,3,7,8-PeCDD ............................................................................... | ...................... | .................... | 200 | 4 |
| 1,2,3,7,8-PeCDF ............................................................................... | ...................... | .................... | 200 | 4 |
| 2,3,4,7,8-PeCDF ............................................................................... | ...................... | .................... | 200 | 4 |
| 1,2,3,4,7,8-HxCDD ............................................................................ | ...................... | .................... | 200 | 4 |
| 1,2,3,6,7,8-HxCDD ............................................................................ | ...................... | .................... | 200 | 4 |
| 1,2,3,7,8,9-HxCDD ............................................................................ | ...................... | .................... | 200 | 4 |
| 1,2,3,4,7,8-HxCDF ............................................................................ | ...................... | .................... | 200 | 4 |
| 1,2,3,6,7,8-HxCDF ............................................................................ | ...................... | .................... | 200 | 4 |
| 1,2,3,7,8,9-HxCDF ............................................................................ | ...................... | .................... | 200 | 4 |
| 2,3,4,6,7,8-HxCDF ............................................................................ | ...................... | .................... | 200 | 4 |
| 1,2,3,4,6,7,8-HpCDD ......................................................................... | ...................... | .................... | 200 | 4 |
| 1,2,3,4,6,7,8-HpCDF ......................................................................... | ...................... | .................... | 200 | 4 |
| 1,2,3,4,7,8,9-HpCDF ......................................................................... | ...................... | .................... | 200 | 4 |
| OCDD ................................................................................................ | ...................... | .................... | 400 | 8 |
| OCDF ................................................................................................ | ...................... | .................... | 400 | 8 |
| 13C12-2,3,7,8-TCDD ........................................................................... | 100 | 2 |  |  |
| 13C12-2,3,7,8-TCDF ........................................................................... | 100 | 2 |  |  |
| 13C12-1,2,3,7,8-PeCDD ..................................................................... | 100 | 2 |  |  |
| 13C12-1,2,3,7,8-PeCDF ...................................................................... | 100 | 2 |  |  |
| 13C12-2,3,4,7,8-PeCDF ...................................................................... | 100 | 2 |  |  |
| 13C12-1,2,3,4,7,8-HxCDD .................................................................. | 100 | 2 |  |  |
| 13C12-1,2,3,6,7,8-HxCDD .................................................................. | 100 | 2 |  |  |
| 13C12-1,2,3,4,7,8-HxCDF ................................................................... | 100 | 2 |  |  |
| 13C12-1,2,3,6,7,8-HxCDF ................................................................... | 100 | 2 |  |  |
| 13C12-1,2,3,7,8,9-HxCDF ................................................................... | 100 | 2 |  |  |
| 13C12-2,3,4,6,7,8-HxCDF ................................................................... | 100 | 2 |  |  |
| 13C12-1,2,3,4,6,7,8-HpCDD ............................................................... | 100 | 2 |  |  |
| 13C12-1,2,3,4,6,7,8-HpCDF ................................................................ | 100 | 2 |  |  |
| 13C12-1,2,3,4,7,8,9-HpCDF ................................................................ | 100 | 2 |  |  |
| 13C12-OCDD ...................................................................................... | 200 | 4 |  |  |

#### Pt. 136, App. A, Meth. 1613

40 CFR Ch. I (7–1–17 Edition)

TABLE 3—CONCENTRATION OF STOCK AND SPIKING SOLUTIONS CONTAINING CDDS/CDFS AND

LABELED COMPOUNDS—Continued

| CDD/CDF | Labeled com- pound stock solution 1 (ng/mL) | Labeled compound spiking solu- tion 2 (ng/mL) | PAR stock solution 3 (ng/mL) | PAR spiking solution 4 (ng/mL) |
| --- | --- | --- | --- | --- |
| Cleanup Standard 5 | 0.8 |  |  |  |
| 37Cl4-2,3,7,8-TCDD ............................................................. |  |  |  |  |
| Internal Standards 6 |  |  |  |  |
| 13C12-1,2,3,4-TCDD ............................................................ | 200 |  |  |  |
| 13C12-1,2,3,7,8,9-HxCDD .................................................... | 200 |  |  |  |

1 Section 7.10—prepared in nonane and diluted to prepare spiking solution.

2 Section 7.10.3—prepared in acetone from stock solution daily.

3 Section 7.9—prepared in nonane and diluted to prepare spiking solution.

4 Section 7.14—prepared in acetone from stock solution daily.

5 Section 7.11—prepared in nonane and added to extract prior to cleanup.

6 Section 7.12—prepared in nonane and added to the concentrated extract immediately prior to injection into the GC (Section 14.2).

TABLE 4—CONCENTRATION OF CDDS/CDFS IN CALIBRATION AND CALIBRATION VERIFICATION SOLUTIONS 1 (SECTION 15.3)

|  | CDD/CDF | CS2 (ng/mL) | CS3 (ng/mL) | CS4 (ng/mL) | CS5 (ng/mL) |
| --- | --- | --- | --- | --- | --- |
| 2,3,7,8-TCDD .............................................................. | 0.5 | 2 | 10 | 40 | 200 |
| 2,3,7,8-TCDF ............................................................... | 0.5 | 2 | 10 | 40 | 200 |
| 1,2,3,7,8-PeCDD ......................................................... | 2.5 | 10 | 50 | 200 | 1000 |
| 1,2,3,7,8-PeCDF ......................................................... | 2.5 | 10 | 50 | 200 | 1000 |
| 2,3,4,7,8-PeCDF ......................................................... | 2.5 | 10 | 50 | 200 | 1000 |
| 1,2,3,4,7,8-HxCDD ...................................................... | 2.5 | 10 | 50 | 200 | 1000 |
| 1,2,3,6,7,8-HxCDD ...................................................... | 2.5 | 10 | 50 | 200 | 1000 |
| 1,2,3,7,8,9-HxCDD ...................................................... | 2.5 | 10 | 50 | 200 | 1000 |
| 1,2,3,4,7,8-HxCDF ...................................................... | 2.5 | 10 | 50 | 200 | 1000 |
| 1,2,3,6,7,8-HxCDF ...................................................... | 2.5 | 10 | 50 | 200 | 1000 |
| 1,2,3,7,8,9-HxCDF ...................................................... | 2.5 | 10 | 50 | 200 | 1000 |
| 2,3,4,6,7,8-HxCDF ...................................................... | 2.5 | 10 | 50 | 200 | 1000 |
| 1,2,3,4,6,7,8-HpCDD ................................................... | 2.5 | 10 | 50 | 200 | 1000 |
| 1,2,3,4,6,7,8-HpCDF ................................................... | 2.5 | 10 | 50 | 200 | 1000 |
| 1,2,3,4,7,8,9-HpCDF ................................................... | 2.5 | 10 | 50 | 200 | 1000 |
| OCDD .......................................................................... | 5.0 | 20 | 100 | 400 | 2000 |
| OCDF .......................................................................... | 5.0 | 20 | 100 | 400 | 2000 |
| 13 C12-2,3,7,8-TCDD .................................................... | 100 | 100 | 100 | 100 | 100 |
| 13 C12-2,3,7,8-TCDF .................................................... | 100 | 100 | 100 | 100 | 100 |
| 13 C12-1,2,3,7,8-PeCDD ............................................... | 100 | 100 | 100 | 100 | 100 |
| 13 C12-PeCDF .............................................................. | 100 | 100 | 100 | 100 | 100 |
| 13 C12-2,3,4,7,8-PeCDF ............................................... | 100 | 100 | 100 | 100 | 100 |
| 13 C12-1,2,3,4,7,8-HxCDD ............................................ | 100 | 100 | 100 | 100 | 100 |
| 13 C12-1,2,3,6,7,8-HxCDD ............................................ | 100 | 100 | 100 | 100 | 100 |
| 13 C12-1,2,3,4,7,8-HxCDF ............................................ | 100 | 100 | 100 | 100 | 100 |
| 13 C12-1,2,3,6,7,8-HxCDF ............................................ | 100 | 100 | 100 | 100 | 100 |
| 13 C12-1,2,3,7,8,9-HxCDF ............................................ | 100 | 100 | 100 | 100 | 100 |
| 13 C12-1,2,3,4,6,7,8-HpCDD ........................................ | 100 | 100 | 100 | 100 | 100 |
| 13 C12-1,2,3,4,6,7,8-HpCDF ......................................... | 100 | 100 | 100 | 100 | 100 |
| 13 C12-1,2,3,4,7,8,9-Hp CDF ........................................ | 100 | 100 | 100 | 100 | 100 |
| 13 C12-OCDD ............................................................... | 200 | 200 | 200 | 200 | 200 |
| Cleanup Standard: |  |  |  |  |  |
| 37 C14-2,3,7,8-TCDD ..................................... | 0.5 | 2 | 10 | 40 | 200 |
| Internal Standards: |  |  |  |  |  |
| 13 C12-1,2,3,4-TCDD .................................................... | 100 | 100 | 100 | 100 | 100 |
| 13 C12-1,2,3,7,8,9-HxCDD ............................................ | 100 | 100 | 100 | 100 | 100 |

TABLE 5—GC RETENTION TIME WINDOW DEFINING SOLUTION AND ISOMER SPECIFICITY TEST STANDARD (SECTION 7.15)

DB–5 column GC retention-time window defining solution

| CDD/CDF | First eluted | Last eluted |
| --- | --- | --- |
| TCDF ............................................................................................. | 1,3,6,8- .............................................. | 1,2,8,9- |
| TCDD ............................................................................................. | 1,3,6,8- .............................................. | 1,2,8,9- |
| PeCDF ........................................................................................... | 1,3,4,6,8- ........................................... | 1,2,3,8,9- |

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1613

TABLE 5—GC RETENTION TIME WINDOW DEFINING SOLUTION AND ISOMER SPECIFICITY TEST STANDARD (SECTION 7.15)—Continued

DB–5 column GC retention-time window defining solution

| CDD/CDF | First eluted | Last eluted |
| --- | --- | --- |
| PeCDD .......................................................................................... | 1,2,4,7,9- ........................................... | 1,2,3,8,9- |
| HxCDF ........................................................................................... | 1,2,3,4,6,8- ........................................ | 1,2,3,4,8,9- |
| HxCDD .......................................................................................... | 1,2,4,6,7,9- ........................................ | 1,2,3,4,6,7- |
| HpCDF ........................................................................................... | 1,2,3,4,6,7,8- ..................................... | 1,2,3,4,7,8,9- |
| HpCDD .......................................................................................... | 1,2,3,4,6,7,9- ..................................... | 1,2,3,4,6,7,8- |

##### DB–5 Column TCDD Specificity Test Standard

1,2,3,7 = 1,2,3,8-TCDD

2,3,7,8-TCDD

1,2,3,9-TCDD

##### DB–225 Column TCDF Isomer Specificity Test Standard

2,3,4,7-TCDF

2,3,7,8-TCDF

1,2,3,9-TCDF

TABLE 6—ACCEPTANCE CRITERIA FOR PERFORMANCE TESTS WHEN ALL CDDS/CDFS ARE TESTED 1

| CDD/CDF | Test conc. (ng/mL) | IPR 2 3 | OPR (ng/mL) | VER (ng/mL) |
| --- | --- | --- | --- | --- |
|  |  | s (ng/mL) | X (ng/mL) |  |  |
| 2,3,7,8-TCDD ........................................................ | 10 | 2.8 | 8.3–12.9 | 6.7–15.8 | 7.8–12.9 |
| 2,3,7,8-TCDF ......................................................... | 10 | 2.0 | 8.7–13.7 | 7.5–15.8 | 8.4–12.0 |
| 1,2,3,7,8-PeCDD ................................................... | 50 | 7.5 | 38–66 | 35–71 | 39–65 |
| 1,2,3,7,8-PeCDF ................................................... | 50 | 7.5 | 43–62 | 40–67 | 41–60 |
| 2,3,4,7,8-PeCDF ................................................... | 50 | 8.6 | 36–75 | 34–80 | 41–61 |
| 1,2,3,4,7,8-HxCDD ................................................ | 50 | 9.4 | 39–76 | 35–82 | 39–64 |
| 1,2,3,6,7,8-HxCDD ................................................ | 50 | 7.7 | 42–62 | 38–67 | 39–64 |
| 1,2,3,7,8,9-HxCDD ................................................ | 50 | 11.1 | 37–71 | 32–81 | 41–61 |
| 1,2,3,4,7,8-HxCDF ................................................ | 50 | 8.7 | 41–59 | 36–67 | 45–56 |
| 1,2,3,6,7,8-HxCDF ................................................ | 50 | 6.7 | 46–60 | 42–65 | 44–57 |
| 1,2,3,7,8,9-HxCDF ................................................ | 50 | 6.4 | 42–61 | 39–65 | 45–56 |
| 2,3,4,6,7,8-HxCDF ................................................ | 50 | 7.4 | 37–74 | 35–78 | 44–57 |
| 1,2,3,4,6,7,8-HpCDD ............................................. | 50 | 7.7 | 38–65 | 35–70 | 43–58 |
| 1,2,3,4,6,7,8-HpCDF ............................................. | 50 | 6.3 | 45–56 | 41–61 | 45–55 |
| 1,2,3,4,7,8,9-HpCDF ............................................. | 50 | 8.1 | 43–63 | 39–69 | 43–58 |
| OCDD .................................................................... | 100 | 19 | 89–127 | 78–144 | 79–126 |
| OCDF .................................................................... | 100 | 27 | 74–146 | 63–170 | 63–159 |
| 13C12-2,3,7,8-TCDD ............................................... | 100 | 37 | 28–134 | 20–175 | 82–121 |
| 13C12-2,3,7,8-TCDF ............................................... | 100 | 35 | 31–113 | 22–152 | 71–140 |
| 13C12-1,2,3,7,8-PeCDD ......................................... | 100 | 39 | 27–184 | 21–227 | 62–160 |
| 13C12-1,2,3,7,8-PeCDF .......................................... | 100 | 34 | 27–156 | 21–192 | 76–130 |
| 13C12-2,3,4,7,8-PeCDF .......................................... | 100 | 38 | 16–279 | 13–328 | 77–130 |
| 13C12-1,2,3,4,7,8-HxCDD ...................................... | 100 | 41 | 29–147 | 21–193 | 85–117 |
| 13C12-1,2,3,6,7,8-HxCDD ...................................... | 100 | 38 | 34–122 | 25–163 | 85–118 |
| 13C12-1,2,3,4,7,8-HxCDF ....................................... | 100 | 43 | 27–152 | 19–202 | 76–131 |
| 13C12-1,2,3,6,7,8-HxCDF ....................................... | 100 | 35 | 30–122 | 21–159 | 70–143 |
| 13C12-1,2,3,7,8,9-HxCDF ....................................... | 100 | 40 | 24–157 | 17–205 | 74–135 |
| 13C12-2,3,4,6,7,8,-HxCDF ...................................... | 100 | 37 | 29–136 | 22–176 | 73–137 |
| 13C12-1,2,3,4,6,7,8-HpCDD ................................... | 100 | 35 | 34–129 | 26–166 | 72–138 |
| 13C12-1,2,3,4,6,7,8-HpCDF .................................... | 100 | 41 | 32–110 | 21–158 | 78–129 |
| 13C12-1,2,3,4,7,8,9-HpCDF .................................... | 100 | 40 | 28–141 | 20–186 | 77–129 |
| 13C12-OCDD .......................................................... | 200 | 95 | 41–276 | 26–397 | 96–415 |
| 37Cl4-2,3,7,8-TCDD ............................................... | 10 | 3.6 | 3.9–15.4 | 3.1–19.1 | 7.9–12.7 |

1 All specifications are given as concentration in the final extract, assuming a 20 L volume.

2 s = standard deviation of the concentration.

3 X = average concentration.

#### Pt. 136, App. A, Meth. 1613

40 CFR Ch. I (7–1–17 Edition)

TABLE 6A—ACCEPTANCE CRITERIA FOR PERFORMANCE TESTS WHEN ONLY TETRA COMPOUNDS ARE

TESTED 1

| CDD/CDF | Test Conc. (ng/mL) | IPR 2 3 | OPR (ng/mL) | VER (ng/mL) |
| --- | --- | --- | --- | --- |
|  |  | s (ng/mL) | X (ng/mL) |  |  |
| 2,3,7,8-TCDD .......................................................... | 10 | 2.7 | 8.7–12.4 | 7.314.6 | 8.2–12.3 |
| 2,3,7,8-TCDF ........................................................... | 10 | 2.0 | 9.1–13.1 | 8.0–14.7 | 8.6–11.6 |
| 13C12-2,3,7,8-TCDD ................................................ | 100 | 35 | 32–115 | 25–141 | 85–117 |
| 13C12-2,3,7,8-TCDF ................................................. | 100 | 34 | 35–99 | 26–126 | 76–131 |
| 37Cl4-2,3,7,8-TCDD ................................................. | 10 | 3.4 | 4.5–13.4 | 3.7–15.8 | 8.3–12.1 |

1 All specifications are given as concentration in the final extract, assuming a 20 L volume.

2 s = standard deviation of the concentration.

3 X = average concentration.

TABLE 7—LABELED COMPOUNDS RECOVERY IN SAMPLES WHEN ALL CDDS/CDFS ARE TESTED

| Compound | Test conc. (ng/mL) | Labeled compound recovery |
| --- | --- | --- |
|  |  | (ng/mL) 1 | (%) |
| 13C12-2,3,7,8-TCDD ..................................................................................................... | 100 | 25–164 | 25–164 |
| 13C12-2,3,7,8-TCDF ..................................................................................................... | 100 | 24–169 | 24–169 |
| 13C12-1,2,3,7,8-PeCDD ............................................................................................... | 100 | 25–181 | 25–181 |
| 13C12-1,2,3,7,8-PeCDF ................................................................................................ | 100 | 24–185 | 24–185 |
| 13C12-2,3,4,7,8-PeCDF ................................................................................................ | 100 | 21–178 | 21–178 |
| 13C12-1,2,3,4,7,8-HxCDD ............................................................................................ | 100 | 32–141 | 32–141 |
| 13C12-1,2,3,6,7,8-HxCDD ............................................................................................ | 100 | 28–130 | 28–130 |
| 13C12-1,2,3,4,7,8-HxCDF ............................................................................................. | 100 | 26–152 | 26–152 |
| 13C12-1,2,3,6,7,8-HxCDF ............................................................................................. | 100 | 26–123 | 26–123 |
| 13C12-1,2,3,7,8,9-HxCDF ............................................................................................. | 100 | 29–147 | 29–147 |
| 13C12-2,3,4,6,7,8-HxCDF ............................................................................................. | 100 | 28–136 | 28–136 |
| 13C12-1,2,3,4,6,7,8-HpCDD ......................................................................................... | 100 | 23–140 | 23–140 |
| 13C12-1,2,3,4,6,7,8-HpCDF .......................................................................................... | 100 | 28–143 | 28–143 |
| 13C12-1,2,3,4,7,8,9-HpCDF .......................................................................................... | 100 | 26–138 | 26–138 |
| 13C12-OCDD ................................................................................................................ | 200 | 34-313 | 17–157 |
| 37Cl4-2,3,7,8-TCDD ..................................................................................................... | 10 | 3.5–19.7 | 35–197 |

1 Specification given as concentration in the final extract, assuming a 20-L volume.

TABLE 7A—LABELED COMPOUND RECOVERY IN SAMPLES WHEN ONLY TETRA COMPOUNDS ARE

TESTED

| Compound | Test conc. (ng/mL) | Labeled compound recovery |
| --- | --- | --- |
|  |  | (ng/mL) 1 | (%) |
| 13C12-2,3,7,8-TCDD ..................................................................................................... | 100 | 31–137 | 31–137 |
| 13C12-2,3,7,8-TCDF ..................................................................................................... | 100 | 29–140 | 29–140 |
| 37Cl4-2,3,7,8-TCDD ..................................................................................................... | 10 | 4.2–16.4 | 42–164 |

1 Specification given as concentration in the final extract, assuming a 20 L volume.

TABLE 8—DESCRIPTORS, EXACT M/Z’S, M/Z TYPES, AND ELEMENTAL COMPOSITIONS OF THE CDDS AND CDFS

| Descriptor | Exact M/Z 1 | M/Z type | Elemental composition | Substance 2 |
| --- | --- | --- | --- | --- |
| 1 ................................. 2 ................................. | 292.9825 303.9016 305.8987 315.9419 317.9389 319.8965 321.8936 327.8847 330.9792 331.9368 333.9339 375.8364 339.8597 341.8567 351.9000 | Lock M M = 2 M M = 2 M M = 2 M QC M M = 2 M = 2 M = 2 M = 4 M = 2 | C7F11 ................................................................. C12H 35Cl4O ...................................................... 4 C12H 35Cl 37ClO ................................................ 4 3 13C12H 35Cl4O ................................................... 4 13C12H 35Cl 37ClO ............................................ 4 3 C12H 35Cl4O2 ..................................................... 4 C12H 35Cl 37ClO2 .............................................. 4 3 C12H 37Cl4O2 ..................................................... 4 C7F13 ................................................................. 13C12H 35Cl4O2 .................................................. 4 13C12H 35Cl 37ClO2 ........................................... 4 3 C12H 35Cl 37ClO ................................................ 4 5 C12H 35Cl 37ClO ................................................ 3 4 C12H 35Cl 37Cl2O .............................................. 3 3 13C12H 35Cl 37ClO ............................................ 3 4 | PFK TCDF TCDF TCDF 3 TCDF 3 TCDD TCDD TCDD 4 PFK TCDD 3 TCDD 3 HxCDPE PeCDF PeCDF PeCDF |

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1613

TABLE 8—DESCRIPTORS, EXACT M/Z’S, M/Z TYPES, AND ELEMENTAL COMPOSITIONS OF THE CDDS

AND CDFS—Continued

| Descriptor | Exact M/Z 1 | M/Z type | Elemental composition | Substance 2 |
| --- | --- | --- | --- | --- |
| 3 ................................. 4 ................................. 5 ................................. | 353.8970 354.9792 355.8546 357.8516 367.8949 369.8919 409.7974 373.8208 375.8178 383.8639 385.8610 389.8157 391.8127 392.9760 401.8559 403.8529 430.9729 445.7555 407.7818 409.7789 417.8253 419.8220 423.7766 425.7737 430.9729 435.8169 437.8140 479.7165 441.7428 442.9728 443.7399 457.7377 459.7348 469.7779 471.7750 513.6775 | M = 4 Lock M = 2 M = 4 M = 2 M = 4 M = 2 M = 2 M = 4 M M = 2 M = 2 M = 4 Lock M = 2 M = 4 QC M = 4 M = 2 M = 4 M M = 2 M = 2 M = 4 Lock M = 2 M = 4 M = 4 M = 2 Lock M = 4 M = 2 M = 4 M = 2 M = 4 M = 4 | 13C12H 35Cl 37Cl2O ........................................... 3 3 C9F13 ................................................................. C12H 35Cl 37ClO2 .............................................. 3 4 C12H 35Cl 37Cl2O2 ............................................. 3 3 13C12H 35Cl 37ClO2 ........................................... 3 4 13C12H 35Cl 37Cl2O2 .......................................... 3 3 C12H 35Cl 37ClO ................................................ 3 6 C12H 35Cl 37ClO ................................................ 2 5 C12H 35Cl 37Cl2O .............................................. 2 4 13C12H 35Cl6O ................................................... 2 13C12H 35Cl 37ClO ............................................ 2 5 C12H 35Cl 37ClO2 .............................................. 2 5 C12H 35Cl 37Cl2O2 ............................................. 2 4 C9F15 ................................................................. 13C12H 35Cl 37ClO2 ........................................... 2 5 13C12H 35Cl 37Cl2O2 .......................................... 2 4 C9F17 ................................................................. C12H 35Cl 37Cl2O .............................................. 2 6 C12H35Cl 37ClO ................................................. 6 C12H35Cl 37Cl2O ................................................ 5 13C12H35Cl7O .................................................... 13C12H35Cl 37ClO .............................................. 6 C12H35Cl 37ClO2 ................................................ 6 C12H35Cl 37Cl2O2 .............................................. 5 C9F17 ................................................................. 13C12H35Cl 37ClO2 ............................................ 6 13C12H35Cl 37Cl2O2 ........................................... 5 C12H35Cl 37Cl2O ................................................ 7 C 35Cl 37ClO .................................................... 12 7 C10F17 ................................................................ C 35Cl 37Cl O .................................................. 12 6 2 C 35Cl 37ClO .................................................. 12 7 2 C 35Cl 37Cl O ................................................. 12 6 2 2 13C 35Cl 37ClO ............................................... 12 7 2 13C 35Cl 37Cl O .............................................. 12 6 2 2 C 35Cl 37Cl O .................................................. 12 8 2 | PeCDF 3 PFK PeCDD PeCDD PeCDD 3 PeCDD 3 HpCDPE HxCDF HxCDF HxCDF 3 HxCDF 3 HxCDD HxCDD PFK HxCDD 3 HxCDD 3 PFK OCDPE HpCDF HpCDF HpCDF 3 HpCDF 3 HpCDD HpCDD PFK HpCDD 3 HpCDD 3 NCDPE OCDF PFK OCDF OCDD OCDD OCDD 3 OCDD 3 DCDPE |

1 Nuclidic masses used: H = 1.007825.

O = 15.994915.

C = 12.00000.

35Cl = 34.968853.

13C = 13.003355.

37Cl = 36.965903.

F = 18.9984.

2 TCDD = Tetrachlorodibenzo-p-dioxin. PeCDD = Pentachlorodibenzo-p-dioxin. HxCDD = Hexachlorodibenzo-p-dioxin. HpCDD = Heptachlorodibenzo-p-dioxin. OCDD = Octachlorodibenzo-p-dioxin. HxCDPE = Hexachlorodiphenyl ether. OCDPE = Octachlorodiphenyl ether.

DCDPE = Decachlorodiphenyl ether. TCDF = Tetrachlorodibenzofuran.

PeCDF = Pentachlorodibenzofuran. HxCDF = Hexachlorodibenzofuran. HpCDF = Heptachlorodibenzofuran. OCDF = Octachlorodibenzofuran. HpCDPE = Heptachlorodiphenyl ether. NCDPE = Nonachlorodiphenyl ether. PFK = Perfluorokerosene.

3 Labeled compound.

4 There is only one m/z for 37Cl4-2,3,7,8,-TCDD (cleanup standard).

TABLE 9—THEORETICAL ION ABUNDANCE RATIOS AND QC LIMITS

| Number of chlorine atoms | M/Z’s forming ratio | Theoretical ratio | QC limit 1 |
| --- | --- | --- | --- |
|  |  |  | Lower | Upper |
| 4 2 .............................................................. | M/(M = 2) ............................................... | 0.77 | 0.65 | 0.89 |
| 5 ................................................................ | (M = 2)/(M = 4) ....................................... | 1.55 | 1.32 | 1.78 |
| 6 ................................................................ | (M = 2)/(M = 4) ....................................... | 1.24 | 1.05 | 1.43 |
| 6 3 .............................................................. | M/(M = 2) ............................................... | 0.51 | 0.43 | 0.59 |
| 7 ................................................................ | (M = 2)/(M = 4) ....................................... | 1.05 | 0.88 | 1.20 |

#### Pt. 136, App. A, Meth. 1613

40 CFR Ch. I (7–1–17 Edition)

TABLE 9—THEORETICAL ION ABUNDANCE RATIOS AND QC LIMITS—Continued

| Number of chlorine atoms | M/Z’s forming ratio | Theoretical ratio | QC limit 1 |
| --- | --- | --- | --- |
|  |  |  | Lower | Upper |
| 7 4 .............................................................. 8 ................................................................ | M/(M = 2) ............................................... (M = 2)/(M = 4) ....................................... | 0.44 0.89 | 0.37 0.76 | 0.51 1.02 |

1 QC limits represent 15% windows around the theoretical ion abundance ratios.

2 Does not apply to 37Cl4-2,3,7,8-TCDD (cleanup standard).

3 Used for 13C12-HxCDF only.

4 Used for 13C12-HpCDF only.

TABLE 10—SUGGESTED SAMPLE QUANTITIES TO BE EXTRACTED FOR VARIOUS MATRICES 1

| Sample Matrix 2 | Example | Percent solids | Phase | Quantity ex- tracted |
| --- | --- | --- | --- | --- |
| Single-phase: | Drinking water ....................... | <1 | (3) .......................................... | 1000 mL. |
| Aqueous .......................... |  |  |  |  |
|  | Groundwater |  |  |  |
|  | Treated wastewater |  |  |  |
| Solid ................................. | Dry soil .................................. | >20 | Solid ...................................... | 10 g. |
|  | Compost |  |  |  |
|  | Ash |  |  |  |
| Organic ............................ | Waste solvent ....................... | <1 | Organic ................................. | 10 g. |
|  | Waste oil |  |  |  |
|  | Organic polymer |  |  |  |
| Tissue .............................. | Fish ....................................... | ........................ | Organic ................................. | 10 g. |
|  | Human adipose |  |  |  |
| Multi-phase: |  |  |  |  |
| Liquid/Solid: |  |  |  |  |
| Aqueous/Solid .......... | Wet soil ................................. | 1–30 | Solid ...................................... | 10 g. |
|  | Untreated effluent. |  |  |  |
|  | Digested municipal sludge. |  |  |  |
|  | Filter cake. |  |  |  |
|  | Paper pulp. |  |  |  |
| Organic/solid ............ | Industrial sludge .................... | 1–100 | Both ....................................... | 10 g. |
|  | Oily waste |  |  |  |
| Liquid/Liquid: |  |  |  |  |
| Aqueous/organic ...... | In-process effluent ................ | <1 | Organic ................................. | 10 g. |
|  | Untreated effluent |  |  |  |
|  | Drum waste |  |  |  |
| Aqueous/organic/ | Untreated effluent ................. | >1 | Organic and solid .................. | 10 g. |
| solid. |  |  |  |  |
|  | Drum waste |  |  |  |

1 The quantity of sample to be extracted is adjusted to provide 10 g of solids (dry weight). One liter of aqueous samples con- taining 1% solids will contain 10 g of solids. For aqueous samples containing greater than 1% solids, a lesser volume is used so that 10 g of solids (dry weight) will be extracted.

2 The sample matrix may be amorphous for some samples. In general, when the CDDs/CDFs are in contact with a multiphase system in which one of the phases is water, they will be preferentially dispersed in or adsorbed on the alternate phase because of their low solubility in water.

3 Aqueous samples are filtered after spiking with the labeled compounds. The filtrate and the materials trapped on the filter are extracted separately, and the extracts are combined for cleanup and analysis.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1613

Pt. 136, App. A, Meth. 1613

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 1613

Pt. 136, App. A, Meth. 1613

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 1613

Pt. 136, App. A, Meth. 1613

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 1613

24.0   Glossary of Definitions and Purposes

These definitions and purposes are specific to this method but have been conformed to common usage as much as possible.

  - Units of weight and Measure and Their Abbreviations.

    - Symbols:

C—degrees Celsius

L—microliter

m—micrometer

<—less than

>—greater than

%—percent

    - Alphabetical abbreviations:

amp—ampere cm—centimeter g—gram h—hour

D—inside diameter in.—inch

L—liter M—Molecular ion m—meter mg—milligram min—minute mL—milliliter mm—millimeter

m/z—mass-to-charge  ratio

#### Pt. 136, App. A, Meth. 1613

N—normal; gram molecular weight of solute divided by hydrogen equivalent of solute, per liter of solution

OD—outside diameter pg—picogram ppb—part-per-billion ppm—part-per-million

ppq—part-per-quadrillion ppt—part-per-trillion

psig—pounds-per-square inch  gauge v/v—volume per unit volume w/v—weight per unit volume

  - Definitions and Acronyms (in Alpha- betical Order).

Analyte—A CDD or CDF tested for by this method. The analytes are listed in Table 1.

Calibration Standard (CAL)—A solution prepared from a secondary standard and/or stock solutions and used to calibrate the re- sponse of the instrument with respect to analyte concentration.

Calibration Verification Standard (VER)— The mid-point calibration standard (CS3) that is used in to verify calibration. See Table 4.

CDD—Chlorinated Dibenzo-p-ioxin—The isomers and congeners of tetra-through octa- chlorodibenzo-p-dioxin.

CDF—Chlorinated Dibenzofuran—The iso- mers and congeners of tetra-through octa- chlorodibenzofuran.

CS1, CS2, CS3, CS4, CS5—See Calibration standards and Table 4.

Field Blank—An aliquot of reagent water or other reference matrix that is placed in a sample container in the laboratory or the field, and treated as a sample in all respects, including exposure to sampling site condi- tions, storage, preservation, and all analyt- ical procedures. The purpose of the field blank is to determine if the field or sample transporting procedures and environments have contaminated the sample.

GC—Gas chromatograph or gas chroma- tography.

GPC—Gel permeation chromatograph  or gel permeation chromatography.

HPLC—High performance liquid chro- matograph or high performance liquid chro- matography.

HRGC—High resolution GC. HRMS—High resolution MS.

IPR—Initial precision and recovery; four aliquots of the diluted PAR standard ana- lyzed to establish the ability to generate ac- ceptable precision and accuracy. An IPR is performed prior to the first time this method is used and any time the method or instru- mentation is modified.

K-D—Kuderna-Danish concentrator; a de- vice used to concentrate the analytes in a solvent.

Laboratory Blank—See method blank. Laboratory Control sample  (LCS)—See on-

going precision and recovery standard (OPR).

Laboratory Reagent Blank—See method blank.

#### 40 CFR Ch. I (7–1–17 Edition)

May—This action, activity, or procedural step is neither required nor prohibited.

May Not—This action, activity, or proce- dural step is prohibited.

Method Blank—An aliquot of reagent water that is treated exactly as a sample in- cluding exposure to all glassware, equip- ment, solvents, reagents, internal standards, and surrogates that are used with samples. The method blank is used to determine if analytes or interferences are present in the laboratory environment, the reagents, or the apparatus.

Minimum Level (ML)—The level at which the entire analytical system must give a rec- ognizable signal and acceptable calibration point for the analyte. It is equivalent to the concentration of the lowest calibration standard, assuming that all method-specified sample weights, volumes, and cleanup proce- dures have been employed.

MS—Mass spectrometer or mass spectrom- etry.

Must—This action, activity, or procedural step is required.

OPR—Ongoing precision and recovery standard (OPR); a laboratory blank spiked with known quantities  of  analytes.  The  OPR is analyzed exactly like a sample. Its purpose is to assure that the results produced by the laboratory remain within the limits speci- fied in this method  for precision and  recov- ery.

PAR—Precision and recovery standard; secondary standard that is diluted and spiked to form the IPR and OPR.

PFK—Perfluorokerosene; the mixture of compounds used to calibrate the exact m/z scale in the HRMS.

Preparation Blank—See method blank.

Primary Dilution Standard—A solution containing the specified analytes that is pur- chased or prepared from stock solutions and diluted as needed to prepare calibration solu- tions and other solutions.

Quality Control Check Sample (QCS)—A sample containing all or a subset of the analytes at known concentrations. The QCS is obtained from a source external to the lab- oratory or is prepared from a source of standards different from the source of cali- bration standards. It is used to check labora- tory performance with test materials pre- pared external to the normal preparation process.

Reagent Water—Water demonstrated to be free from the analytes of interest and poten- tially interfering substances at the method detection limit for the analyte.

Relative Standard Deviation (RSD)—The standard deviation times 100 divided by the mean. Also termed  ‘‘coefficient  of  vari- ation.’’

RF—Response factor. See Section 10.6.1. RR—Relative response. See Section 10.5.2. RSD—See relative standard deviation.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1624

SDS—Soxhlet/Dean-Stark extractor; an ex- traction device applied to the extraction of solid and semi-solid materials (Reference 7). Should—This  action,  activity,  or  proce-

dural step is suggested but not required.

SICP—Selected   ion   current   profile;   the line described by the signal at an exact m/z. SPE—Solid-phase   extraction;   an   extrac- tion  technique  in  which  an  analyte  is  ex- tracted from an aqueous sample by passage over or through a material capable of revers- ibly adsorbing the analyte. Also termed liq-

uid-solid extraction.

Stock Solution—A  solution containing an analyte that is prepared using a reference material traceable to EPA, the National In- stitute of Science and Technology (NIST), or a source that will attest to the purity and authenticity of the reference material.

TCDD—Tetrachlorodibenzo-p-dioxin. TCDF—Tetrachlorodibenzofuran.

VER—See calibration verification stand- ard.

METHOD 1624 REVISION B—VOLATILE ORGANIC COMPOUNDS  BY  ISOTOPE  DILUTION  GC/MS

- Scope and Application

  - This method is designed to determine the volatile toxic organic pollutants associ- ated with the 1976 Consent Decree and addi- tional compounds amenable  to  purge  and trap gas chromatography-mass spectrometry (GC/MS).

  - The chemical  compounds  listed  in table 1 may be determined in municipal and industrial discharges by this method. The methmd is designed to meet the survey re- quirements of Effluent Guidelines Division (EGD) and the  National  Pollutants  Dis- charge Elimination  System (NPDES)  under 40 CFR 136.1 and 136.5. Any modifications of this method, beyond those expressly per- mitted, shall be considered as major modi- fications subject to application and approval of  alternate  test  procedures  under  40  CFR

136.4 and 136.5.

  - The detection limit of this method is usually dependent on the level of inter- ferences rather than instrumental limita- tions. The limits in table 2 represent the minimum quantity that can be detected with no interferences present.

  - The GC/MS portions of this method are for use only by analysts experienced with GC/MS or under the close supervision of such qualified persons. Laboratories unfamiliar with the analyses of environmental  samples by GC/MS should run the performance tests in reference 1 before beginning.

- Summary of Method

  - Stable isotopically  labeled  analogs  of the compounds of interest are added  to  a  5 mL water sample. The sample is purged at 20–25 C with an inert gas in a specially de- signed   chamber.   The   volatile   organic   com-

pounds are transferred from the aqueous phase into the gaseous phase where they are passed into a sorbent column and trapped. After purging is completed, the trap is backflushed and heated rapidly to desorb the compounds into a gas chromatograph (GC). The compounds are separated by the GC and detected by a mass spectrometer (MS) (ref- erences 2 and 3). The labeled compounds serve to correct the variability of the analyt- ical  technique.

  - Identification of a compound (quali- tative analysis) is performed by comparing the GC retention time and the background corrected characteristic spectral  masses with those of authentic standards.

  - Quantitative analysis is performed by GC/MS using extracted ion current profile (EICP) areas. Isotope dilution is used when labeled compounds are available; otherwise, an internal standard method is used.

  - Quality is assured through reproduc- ible calibration and testing of the purge and trap and GC/MS systems.

- Contamination and Interferences

  - Impurities in the purge gas, organic compounds out-gassing from the plumbing upstream of the trap, and solvent  vapors  in the laboratory account for the majority of contamination problems. The analytical sys- tem is demonstrated to be free from inter- ferences under conditions of the analysis by analyzing blanks initially and with each sample lot (samples analyzed on the same 8 hr shift), as described in Section 8.5.

  - Samples can be contaminated by diffu- sion of volatile organic compounds (particu- larly methylene chloride) through the bottle seal during shipment and storage. A field blank prepared from reagent water and car- ried through the sampling and handling pro- tocol serves as a check on such contamina- tion.

  - Contamination  by   carry-over   can occur when high level and low level  samples are analyzed sequentially. To  reduce  carry- over, the purging device and sample  syringe are rinsed between samples with reagent water. When an unusually concentrated sam- ple is encountered,  it  is  followed  by  analysis of a reagent water blank to check for carry- over. For samples containing  large  amounts of water soluble materials, suspended solids, high boiling compounds, or high levels or purgeable compounds, the purge device is washed with soap solution, rinsed with tap and distilled water, and dried in an oven at 100–125 C. The trap and other parts of the system are also subject to contamination; therefore,  frequent  bakeout  and  purging  of the  entire  system  may  be  required.

  - Interferences resulting from samples will vary considerably from source to source, depending on the diversity of the industrial complex or municipality being sampled.

#### Pt. 136, App. A, Meth. 1624

- Safety

  - The toxicity or carcinogenicity of each compound or reagent used in this meth- od has not been precisely determined; how- ever, each chemical compound should be treated as a potential health hazard. Expo- sure to these compounds should be reduced to the lowest possible level. The laboratory is responsible for maintaining a current awareness file of OSHA regulations regard- ing the safe handling of the chemicals speci- fied in this method. A reference file of data handling sheets should also be made avail- able to all personnel involved in these anal- yses. Additional information on laboratory safety can be found in references 4–6.

  - The following compounds covered by this method have been tentatively classified as known or suspected human or mammalian carcinogens: benzene, carbon tetrachloride, chloroform, and vinyl chloride. Primary standards of these toxic compounds should be prepared in a hood, and a NIOSH/MESA approved toxic gas respirator should be worn when high concentrations are handled.

- Apparatus and Materials

  - Sample bottles for discrete sampling.

    - Bottle—25 to 40 mL with screw cap (Pierce 13075, or equivalent). Detergent wash, rinse  with  tap  and  distilled  water,  and  dry  at

>105 C for one hr minimum before use.

    - Septum—Teflon-faced	silicone (Pierce 12722, or equivalent), cleaned as above and baked at 100–200 C, for one hour minimum.

  - Purge and trap device—consists of purging device, trap, and desorber. Complete devices are commercially available.

    - Purging device—designed to accept 5 mL samples with water column at least 3 cm deep. The volume of the gaseous head space between the water and trap shall be less than 15 mL. The purge gas shall be introduced less than 5 mm from the base of the water  col- umn and shall pass through the water as bubbles with a diameter less than 3 mm. The purging device shown in Figure 1 meets these criteria.

    - Trap—25 to 30 cm 2.5 mm i.d. min- imum,  containing  the  following:

      - Methyl silicone packing—one 0.2 cm, 3 percent OV–1 on 60/80 mesh Chromosorb W,  or  equivalent.

      - Porous polymer—15 1.0 cm, Tenax GC (2,6-diphenylene oxide polymer), 60/80 mesh,  chromatographic  grade,  or   equivalent.

      - Silica gel—8 1.0 cm, Davison Chemical, 35/60 mesh, grade 15, or equivalent. The trap shown in Figure 2 meets these spec- ifications.

    - Desorber—shall   heat   the  trap to 175

5 C in 45 seconds or less. The polymer sec- tion of the trap shall not exceed 180 C, and the remaining sections  shall not exceed  220

#### 40 CFR Ch. I (7–1–17 Edition)

C. The desorber shown in Figure 2 meets these  specifications.

    - The purge and trap device may be a separate unit or coupled to a GC as shown in Figures 3 and 4.

  - Gas chromatograph—shall be linearly temperature programmable with initial and final holds, shall contain a glass jet sepa- rator as the MS interface, and shall produce results which meet the calibration  (Section 7), quality assurance (Section 8), and per- formance tests (Section 11) of this method.

5.3.1 Column—2.8 0.4 m 2 0.5 mm i. d. glass, packekd with one percent SP–1000 on Carbopak B, 60/80 mesh, or equivalent.

  - Mass spectrometer—70  eV  electron  im- pact  ionization;  shall  repetitively  scan   from 20 to 250 amu every 2–3 seconds, and produce a unit resolution (valleys between m/z 174–176 less  than  10  percent  of  the  height  of  the  m/z

175 peak), background corrected mass spec- trum from 50 ng 4-bromo-fluorobenzene (BFB) injected into the GC. The BFB spec- trum shall meet the  mass-intensity  criteria in Table 3. All portions of the GC column, transfer lines, and separator which connect the GC column to the ion source shall re- main at or above the column temperature during analysis to preclude condensation of less volatile compounds.

  - Data system—shall collect and record MS data, store mass intensity data in  spec- tral libraries, process GC/MS data and gen- erate reports, and shall calculate and record response factors.

    - Data acquisition—mass spectra shall be collected continuously throughout the analysis and stored on a mass storage device.

    - Mass spectral libraries—user created libraries containing mass spectra obtained from analysis of authentic standards shall be employed to  reverse search  GC/MS runs  for the compounds of interest (Section 7.2).

    - Data processing—the data system shall be used to search, locate, identify, and quantify the compounds of interest in each GC/MS analysis. Software routines shall be employed to compute retention times and EICP areas. Displays of spectra, mass chromatograms, and library comparisons are required to verify results.

    - Response factors and multipoint calibrations—the data system shall  be  used to record and maintain lists of response fac- tors (response ratios for isotope dilution) and generate multi-point calibration curves (Sec- tion 7). Computations of relative standard deviation (coefficient of variation) are useful for  testing  calibration  linearity.  Statistics on initial and on-going performance shall be maintained (Sections 8 and 11).

  - Syringes—5 mL glass hypodermic, with Luer-lok tips.

  - Micro syringes—10, 25, and 100 uL.

  - Syringe valves—2-way, with Luer ends (Telfon or Kel-F).

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1624

  - Syringe—5 mL, gas-tight, with shut- off valve.

  - Bottles—15 mL., screw-cap with Telfon liner.

  - Balance—analytical, capable of weighing 0.1 mg.

- Reagents and Standards

  - Reagent water—water in which the compounds of interest and interfering com- pounds are not detected by this method (Sec- tion 11.7). It may be generated by any of the following methods:

    - Activated carbon—pass tap water through a carbon bed (Calgon Filtrasorb-300, or equivalent).

    - Water purifier—pass tap water through a purifier (Millipore Super Q, or equivalent).

    - Boil and purge—heat tap water to 90– 100 C and bubble contaminant free inert gas through it for approx one hour. While still hot, transfer the water to screw-cap bottles and seal with a Teflon-lined cap.

  - Sodium thiosulfate—ACS granular.

  - Methanol—pesticide quality or equiva- lent.

  - Standard solutions—purchased as so- lution or mixtures with certification to their purity, concentration, and authenticity, or prepared from materials of known purity and composition. If compound purity is 96 per- cent or  greater,  the  weight  may  be  used without correction to calculate the con- centration of the standard.

  - Preparation of stock solutions—pre- pare in  methanol using  liquid  or gaseous standards per the steps below. Observe the safety precautions given in Section 4.

6.5.1   Place approx 9.8 mL of methanol in a

10 mL ground glass stoppered volumetric flask. Allow the flask to stand  unstoppered for approximately 10 minutes or until all methanol wetted surfaces have dried. In each case, weigh the flask, immediately add the compound, then immediately reweigh to pre- vent evaporation losses from affecting the measurement.

      - Liquids—using   a   100   L   syringe,

permit 2 drops of liquid to fall into the meth- anol without contacting the  leck  of  the flask. Alternatively, inject a  known  volume of the compound into the methanol in the flask using a micro-syringe.

      - Gases	(chloromethane, bromomethane, chloroethane, vinyl chlo- ride)—fill a valved 5 mL gas-tight syringe with the compound. Lower the needle to ap- proximately 5 mm above the methanol me- niscus. Slowly introduce the  compound above the surface of the meniscus. The  gas will dissolve rapidly in the methanol.

    - Fill the  flask  to volume,  stopper, then mix by inverting several times. Cal- culate the concentration in mg/mL (g/L) from the weight gain (or density if a known volume was injected).

    - Transfer the stock solution to a Tef- lon sealed screw-cap-bottle. Store, with minimal  headspace,  in  the  dark  at  ¥10  to

¥20 C.

    - Prepare fresh standards weekly for the gases and 2-chloroethylvinyl ether. All other standards are replaced after one month, or sooner if comparison with check standards indicate a change in concentra- tion. Quality control check standards that can be used to determine the accuracy of calibration standards are available from the US Environmental Protection Agency, Envi- ronmental Monitoring and Support Labora- tory, Cincinnati, Ohio.

  - Labeled compound spiking solution— from stock standard solutions prepared as above, or from mixtures, prepare the spiking solution  to  contain   a   concentration   such that a 5–10 L spike into each 5 mL sample, blank, or aqueous standard analyzed will re- sult in a concentration of 20 g/L of each la- beled compound. For the gases and for the water soluble compounds (acrolein, acrylo- nitrile, acetone, diethyl ether, and MEK), a concentration of 100 g/L may be used. In- clude the internal standards (Section 7.5) in this solution so that a concentration of 20 g/ L in each sample, blank, or aqueous  standard will be produced.

  - Secondary standards—using stock so- lutions, prepare a secondary standard in methanol to contain each pollutant at a con- centration of 500 g/mL For the gases and water soluble compounds (Section 6.6), a con- centration of 2.5 mg/mL may be used.

    - Aqueous calibration  standards— using a 25 L syringe, add 20 L of the sec- ondary standard (Section 6.7) to 50, 100, 200, 500, and 1000 mL of reagent water to produce concentrations of 200, 100, 50, 20, and 10 g/L, respectively. If the higher concentration standard for  the gases  and water  soluble compounds was chosen (Section 6.6), these compounds will be at concentrations of 1000, 500, 250, 100, and 50 g/L in the aqueous cali- bration standards.

    - Aqueous performance standard—an aqueous standard containing all pollutants, internal standards, labeled compounds,  and BFB is prepared  daily,  and  analyzed  each shift to demonstrate  performance  (Section 11).  This  standard  shall  contain  either  20  or

100 g/L of the labeled and pollutant gases and water soluble compounds, 10 g/L BFB, and 20 g/L of all other pollutants, labeled compounds, and internal standards. It  may be the nominal 20 g/L aqueous calibration standard (Section 6.7.1).

    - A  methanolic   standard   containing all pollutants and internal standards is pre- pared to demonstrate recovery of these com- pounds when syringe injection and purge and trap analyses are compared. This standard shall contain either 100 g/mL or 500 g/mL of the gases and water soluble compounds, and  100  g/mL  of  the  remaining  pollutants

#### Pt. 136, App. A, Meth. 1624

and internal standards (consistent with the amounts in the aqueous performance stand- ard in 6.7.2).

    - Other standards which may be need- ed are those for test of BFB performance (Section 7.1) and for collection of mass spec- tra for storage in spectral libraries (Section 7.2).

- Calibration

  - Assemble the gas chromatographic ap- paratus and establish operating conditions given in table  2. By injecting  standards into the GC, demonstrate that the analytical sys- tem meets the detection limits in table 2 and the mass-intensity criteria in table  3  for  50 ng  BFB.

  - Mass spectral libraries—detection and identification of the compound of interest are dependent upon the spectra stored in user created libraries.

7.2.1   Obtain a mass spectrum of each pol- lutant and labeled compound and each inter- nal    standard    by    analyzing    an    authentic standard  either  singly  or  as  part  of  a  mix- ture  in  which  there  is  no  interference  be- tween  closely  eluted  components.  That  only a  single  compound  is  present  is  determined by  examination  of  the  spectrum.  Fragments not   attributable   to   the   compound   under study indicate the presence of an interfering compound.  Adjust  the  analytical  conditions and scan rate (for this test only) to produce an   undistorted   spectrum   at   the   GC   peak maximum.    An    undistorted    spectrum    will usually  be  obtained  if  five  complete  spectra are collected across the upper half of the GC peak.  Software  algorithms  designed  to  ‘‘en- hance’’  the  spectrum  may  eliminate  distor- tion, but may also eliminate authentic m/z’s or introduce other distortion.

    - The authentic reference spectrum is obtained under BFB tuning conditions (Sec- tion 7.1 and table 3) to normalize it to spec- tra from other instruments.

    - The spectrum is edited by saving the

5 most intense mass spectral peaks and all other mass spectral peaks greater than 10 percent of the base peak. This spectrum is stored for reverse search and for compound confirmation.

  - Assemble the purge and trap device. Pack the trap as shown in Figure 2 and con- dition overnight at 170–180 C  by backflushing with an inert gas at a flow rate of 20–30 mL/min. Condition traps daily for a minimum of 10 minutes prior to use.

    - Analyze the aqueous performance standard (Section 6.7.2) according to the purge and trap procedure in Section 10. Com- pute the area at the primary m/z (table 4) for each compound. Compare these areas to those obtained by injecting one L of the methanolic standard (Section 6.7.3) to deter- mine compound recovery. The recovery shall be greater than 20 percent for the water solu- ble  compounds,  and  60–110  percent  for  all

#### 40 CFR Ch. I (7–1–17 Edition)

other compounds. This recovery is dem- onstrated initially for each purge and trap GC/MS system. The test is repeated  only  if the purge and trap or GC/MS systems are modified in any way that might result in a change in recovery.

    - Demonstrate that 100 ng toluene (or toluene-d8) produces an area at m/z 91 (or 99) approx one-tenth that required to exceed the linear range of the system. The exact value must be determined by experience for each instrument. It is used to match the calibra- tion range of the instrument to the analyt- ical range and detection limits required.

  - Calibration by isotope dilution—the isotope dilution approach is used for the purgeable organic compounds when appro- priate labeled compounds are available and when interferences do not preclude the anal- ysis. If labeled compounds are not available, or interferences are present, internal stand- ard methods (Section 7.5 or 7.6) are used. A calibration curve encompassing the con- centration range of interest is prepared for each compound determined. The relative re- sponse (RR) vs concentration (g/L) is plot- ted or computed using a  linear  regression. An example of a calibration curve for tol- uene using toluene-d8 is given in figure 5. Also shown are the 10 percent error limits (dotted lines). Relative response is deter- mined according to the procedures described below. A minimum of five data points are re- quired for calibration (Section 7.4.4).

    - The relative response (RR) of pollut- ant to labeled compound is determined from isotope ratio values calculated from acquired data. Three isotope ratios are used in this process:

RX = the isotope ratio measured in the pure pollutant (figure 6A).

Ry = the isotope ratio of pure labeled com- pound (figure 6B).

Rm = the isotope ratio measured in the ana- lytical mixture of the pollutant and la- beled compounds (figure 6C).

The correct way to calculate RR is: RR = (Ry¥Rm) (RX + 1)/(Rm¥RX)(Ry + 1) If Rm is not between 2Ry and 0.5RX, the method does not apply and the sample is analyzed by internal or external standard methods (Section 7.5 or 7.6).

    - In most cases, the retention times of the pollutant and labeled compound are the same and isotope ratios (R’s) can be cal- culated from the  EICP  areas,  where:  R  = (area at m1/z)/(area at m2/z) If either of the areas is zero, it is assigned a value of one in the calculations; that is, if: area of m1/z = 50721, and area of m2/z = 0, then R = 50721/1 = 50720. The m/z’s are always selected such that RX>Ry. When there is a difference in reten- tion times (RT) between the pollutant and labeled compounds, special precautions are required to determine the isotope ratios.

RX, Ry, and Rm are defined as follows:

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1624

RX=[area m1/z (at RT1)]/1 Ry = 1/[area m2/z (at RT2)]

Rm=[area m1/z (at RT1)]/[area m2/z (at RT2)]

    - An example of the above calculations can be  taken  from  the  data  plotted  in  figure 6 for toluene and toluene-d8.  For  these  data, RX = 168920/1 = 168900, Ry = 1/60960 = 0.00001640, and Rm = 96868/82508 = 1.174. The RR for the above data is then calculated using the equa- tion given in Section 7.4.1.  For  the  example, RR = 1.174.

NOTE: Not all labeled compounds elute be- fore their pollutant analogs.

    - To  calibrate  the  analytical  system by isotope dilution, analyze  a  5  mL  aliquot of each of the aqueous calibration standards (Section 6.7.1) spiked with an appropriate constant amount of the labeled compound spiking solution (Section 6.6), using the purge and trap procedure in section 10. Com- pute the RR at each concentration.

    - Linearity—if the  ratio  of  relative  re- sponse to concentration for any compound is constant (less than 20 percent coefficient of variation) over the 5 point calibration range, an averaged relative response/concentration ratio may be used for that compound; other- wise, the complete calibration curve for that compound shall be used over the 5 point cali- bration range.

  - Calibration by internal standard—used when criteria for isotope dilution (Section 7.4) cannot be met. The method is applied to pollutants having no labeled analog and  to the labeled compounds. The internal stand- ards used for volatiles analyses are bromochloromethane,	2-bromo-1- chloropropane, and 1,4-dichlorobutane. Con- centrations of the labeled compounds and pollutants without labeled analogs are com- puted relative to the nearest eluted internal standard, as shown in table 2.

    - Response factors—calibration re- quires the determination of response factors (RF) which are defined by the following equation:

RF = (AsxCis)/(AisxCs), where As is the EICP area at the characteristic m/z for the com- pound in the daily standard. Ais is the EICP area at the characteristic m/z for the inter- nal standard.

Cis is the concentration (ug/L) of the inter- nal standard

Cs is the concentration of the pollutant in the daily standard.

    - The response factor is determined at 10, 20, 50, 100, and 200 ug/L for the pollutants (optionally at five times these  concentra- tions for gases and water soluble pollut- ants—see Section 6.7), in a way analogous to that for calibration by isotope dilution (Sec- tion 7.4.4). The RF is plotted against con- centration for each compound in the stand- ard (Cs) to produce a calibration curve.

    - Linearity—if   the   response   factor

(RF) for any compound is constant (less than 35 percent coefficient of variation) over the 5

point calibration range, an averaged re- sponse factor may be used for that com- pound; otherwise, the complete calibration curve for that compound shall be used over the 5 point range.

  - Combined calibration—by adding the isotopically labeled compounds and internal standards (Section 6.6) to the aqueous cali- bration standards (Section 6.7.1), a single set of analyses can be used to produce calibra- tion curves for the isotope dilution and in- ternal standard methods. These curves are verified each shift (Section 11.5) by purging the aqueous performance standard (Section 6.7.2). Recalibration is required only if cali- bration and on-going performance (Section 11.5) criteria cannot be met.

- Quality Assurance/Quality Control

  - Each laboratory that uses this method is required to operate a formal quality assur- ance program. The minimum requirements of this program consist of an initial dem- onstration of laboratory capability, analysis of samples spiked with labeled compounds to evaluate and document data quality, and analysis of standards and blanks as tests of continued performance. Laboratory perform- ance is compared to established performance criteria to determine if the results of anal- yses meet the performance characteristics of the method.

    - The analyst shall make an initial demonstration of the ability to generate ac- ceptable accuracy and precision with this method. This ability is established as de- scribed in Section 8.2.

    - The analyst is permitted to modify this method to improve separations or lower the costs of measurements, provided all per- formance specifications are met. Each time a modification is made to the method, the ana- lyst is required to repeat the procedure in Section 8.2 to demonstrate method perform- ance.

    - Analyses of blanks are required to demonstrate freedom from contamination and that the compounds of interest and interfering compounds have not been carried over from a previous analysis (Section 3). The procedures and criteria for analysis of a blank are described in Sections 8.5 and 11.7.

    - The laboratory shall spike all sam- ples with labeled compounds to monitor method performance. This test  is  described in Section 8.3. When results of these spikes indicate atypical method performance for samples, the samples are diluted to bring method performance within acceptable lim- its (Section 14.2).

    - The laboratory shall, on an on-going basis, demonstrate through the analysis of the aqueous performance standard (Section 6.7.2) that  the analysis  system is  in control. This procedure is described in Sections 11.1 and 11.5.

#### Pt. 136, App. A, Meth. 1624

    - The laboratory shall  maintain records to define the quality of data that is generated. Development of accuracy state- ments is described in Sections 8.4 and 11.5.2.

  - Initial precision and accuracy—to es- tablish the ability to generate acceptable precision and accuracy, the analyst shall perform the following operations:

    - Analyze two sets of four 5–mL aliquots (8 aliquots total) of the aqueous per- formance standard (Section 6.7.2)  according to the method beginning in Section 10.

    - Using results of the first set of four analyses in Section 8.2.1, compute the aver-

age recovery (X¯ ) in g/L and the standard de-

viation of the recovery (s) in g/L for each compound, by isotope dilution for polluitants with a labeled analog, and by in- ternal standard for labeled compounds and pollutants with no labeled analog.

    - For each compound, compare s and X¯

with the corresponding limits for initial pre- cision and accuracy found in table 5. If s and

X¯ for all compounds meet the acceptance cri-

teria, system performance is acceptable and analysis of blanks and samples may begin. If

individual X¯  falls outside the range for accu-

racy, system  performance  is  unacceptable for that compound.

NOTE: The large number of compounds in table 5 present a substantial probability that one or more will fail one of the acceptance criteria when all compoulds are analyzed. To determine if the analytical system is out of control, or if the failure can be attributed to probability, proceed as follows:

    - Using the results of the second set of four  analyses,  compute  s  and  X¯   for  only

those compounds which failed the test of the first set  of four  analyses (Section 8.2.3).  If these compounds now pass, system perform- ance is acceptable for all compounds and analysis of blanks and samples may begin. If, however, any of the same compounds fail again, the analysis system is not performing properly for the compound(s) in question. In this event, correct the problem and repeat the entire test (Section 8.2.1).

  - The laboratory shall spike all samples with labeled compounds to assess method performance on the sample matrix.

    - Spike and analyze each sample ac- cording to the method beginning in  Section 10.

    - Compute the percent recovery (P) of the labeled compounds using the internal standard method (Section 7.5).

    - Compare the percent recovery for each compound with the corresponding la- beled compound recovery limit in table 5. If the recovery of any compound falls outside its warning limit, method performance is un- acceptable for that compound in that sam- ple. Therefore, the sample matrix is complex and the sample is to be diluted and reana- lyzed, per Section 14.2.

#### 40 CFR Ch. I (7–1–17 Edition)

  - As part of the QA program for the lab- oratory, method accuracy for wastewater samples shall be assessed and  records  shall be maintained. After  the analysis  of five wastewater samples for which the labeled compounds pass the tests in Section 8.3.3, compute the  average  percent  recovery  (P) and the standard deviation of the percent re- covery (sp) for the labeled compounds only. Express the  accuracy  assessment  as  a  per- cent recovery interval from P¥2sp to P  +  2sp. For example, if P = 90% and sp = 10%, the ac- curacy interval is expressed as 70–110%. Up- date the accuracy assessment for each com- pound on a regular basis (e.g. after each 5–10 new  accuracy  measurements).

  - Blanks—reagent water blanks are ana- lyzed to demonstrate freedom from carry- over (Section 3) and contamination.

    - The level at which the purge and trap system will carry greater than 5 g/L of a pollutant of interest (table 1) into a suc- ceeding blank shall be determined by ana- lyzing successively larger concentrations of these compounds. When a sample contains this concentration or more, a blank shall be analyzed immediately following this  sample to demonstrate no carry-over at the 5 g/L level.

    - With each sample lot (samples ana- lyzed on the same 8 hr shift), a blank shall be analyzed immediately after analysis of the aqueous performance standard (Section  11.1) to  demonstrate  freedom  from   contamina- tion. If any of  the  compounds  of  interest (table 1) or any potentially interfering com- pound  is  found  in  a  blank  at  greater  than  10

g/L (assuming a response factor of 1 relative to the nearest eluted internal standard for compounds not listed in table 1), analysis of samples is halted until the source of con- tamination is eliminated and a  blank  shows no evidence of contamination at this level.

  - The specifications contained in this method can be met if the apparatus used is calibrated properly, then maintained in a calibrated state.

The standards used for calibration (Section 7), calibration verification (Section 11.5) and for initial (Section 8.2) and on-going (Section 11.5) precision and accuracy should be iden- tical, so that the most precise results will be obtained. The GC/MS instrument in par- ticular will provide the most reproducible re- sults if dedicated to the settings and condi- tions required for the analyses  of  volatiles by this method.

  - Depending on specific program re- quirements, field replicates may be collected to determine the precision of the sampling technique, and spiked samples may be re- quired to determine the accuracy of the analysis when internal or external standard methods are used.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1624

- Sample Collection, Preservation, and Handling

  - Grab samples are collected in glass containers having a total volume greater than 20 mL. Fill sample bottles so that no air bubbles pass through the sample as the bottle is filled. Seal each  bottle  so  that  no air bubbles are entrapped. Maintain the her- metic seal on the sample bottle until time of analysis.

  - Samples are maintained at 0–4 C from the time of collection until analysis. If  the sample contains residual chlorine, add  so- dium thiosulfate preservative (10  mg/40  mL) to the empty sample bottles just prior to shipment   to   the   sample   site.   EPA   Methods

330.4 and 330.5 may be used for measurement of residual chlorine (Reference 8). If preserv- ative has been added, shake bottle vigor- ously for one minute immediately after fill- ing.

  - Experimental evidence indicates that some aromatic compounds, notably benzene, toluene, and ethyl benzene are susceptible to rapid biological degradation under certain environmental  conditions.  Refrigeration alone may not be adequate to preserve these compounds in wastewaters for more than seven days. For this reason, a separate sam- ple should be collected, acidified, and ana- lyzed when these aromatics are to be deter- mined. Collect about 500 mL of sample in a clean  container.

Adjust the pH of the sample to about 2 by adding HCl (1 + 1) while stirring. Check pH with narrow  range  (1.4  to  2.8)  pH  paper.  Fill a   sample   container   as   described   in   Section

9.1. If residual chlorine is present, add so- dium thiosulfate to a separate sample con- tainer and fill as in Section 9.1.

  - All samples shall be analyzed within 14 days of collection.

- Purge, Trap, and GC/MS Analysis

  - Remove standards and samples from cold storage and bring to 20–25 .

  - Adjust the purge gas flow rate to 40 4 mL/min. Attach the trap inlet to the purging device and  set the  valve to  the purge  mode (figure 3). Open the syringe valve located on the purging device sample introduction nee- dle (figure 1).

  - Remove the plunger from a 5–mL sy- ringe and attach a closed syringe valve. Open the sample bottle and carefully pour the sample into  the  syringe  barrel  until  it  over- flows. Replace the plunger and compress the sample. Open the syringe valve and vent any residual air while adjusting the sample vol- ume to 5.0 mL. Because this process of tak- ing an aliquot destroys the validity of the sample for future analysis, fill a second sy- ringe at this time to protect against possible loss of data. Add an appropriate  amount  of the labeled compound spiking solution (Sec-

tion 6.6) through the valve bore, then close the valve.

  - Attach the syringe valve assembly to the syringe valve on  the  purging  device. Open both syringe valves and inject the sam- ple into the purging chamber.

  - Close both valves and purge the  sam- ple for 11.0 0.1 minutes at 20–25 C.

  - After the  11 minute purge time,  at- tach the trap to the chromatograph  and  set the purge and trap apparatus to the desorb mode (figure 4). Desorb the trapped com- pounds into the GC column by heating the trap to 170–180 C while backflushing with carrier gas at 20–60 mL/min for four minutes. Start MS data acquisition upon start of the desorb cycle, and start the GC column tem- perature program 3 minutes later. Table 1 summarizes the recommended operating con- ditions for the gas  chromatograph.  Included in this table are retention times and detec- tion limits that were achieved under these conditions. Other columns may be used pro- vided the requirements in Section 8 can be met. If the priority pollutant  gases  produce GC peaks so broad that the precision and re- covery specifications (Section 8.2) cannot be met, the column may  be  cooled  to  ambient or sub-ambient  temperatures  to  sharpen these  peaks.

  - While analysis of the desorbed com- pounds proceeds, empty the purging chamber using the sample introduction syringe. Wash the chamber with two 5-mL portions of rea- gent water. After the purging device has been emptied, allow the purge gas to vent through the chamber until the frit is dry, so that it is ready for the next sample.

  - After desorbing the sample for four minutes, recondition the trap  by  returning to the purge mode. Wait 15 seconds, then close the syringe valve on the purging device to begin gas flow through the trap. Maintain the trap temperature at 170–180 C. After ap- proximately seven minutes, turn off the trap heater and open the syringe valve to stop the gas flow through the trap. When cool, the trap is ready for the next sample.

- System Performance

  - At the beginning of each 8 hr shift during which analyses are performed, system calibration and performance shall be verified for all  pollutants  and  labeled  compounds. For these tests, analysis of the aqueous per- formance standard (Section 6.7.2) shall be used to verify all performance criteria. Ad- justment and/or recalibration (per Section 7) shall be performed until all performance cri- teria are met. Only after all performance cri- teria are met may blanks and samples be analyzed.

  - BFB  spectrum  validity—the  criteria in table 3 shall be met.

  - Retention times—the absolute reten- tion times of all compounds shall approxi- mate those given in Table 2.

#### Pt. 136, App. A, Meth. 1624

  - GC resolution—the valley height be- tween toluene and toluene-d8 (at m/z 91 and

99 plotted on  the same  graph) shall  be less than 10  percent of  the taller  of  the two peaks.

  - Calibration verification and on-going precision and accuracy—compute the con- centration of each polutant (Table 1) by iso- tope dilution (Section 7.4) for those compmunds which have labeled analogs. Compute the concentration of each pollutant (Table 1) which has no labeled analog by the internal standard method (Section 7.5). Com- pute the concentration of the labeled com- pounds by the internal standard method. These concentrations are computed based on the calibration data determined in Section 7.

    - For each pollutant and labeled com- pound, compare the concentration with the corresponding limit for on-going accuracy in Table 5. If all compmunds meet the accept- ance criteria, system performance is accept- able and analysis of blanks and samples may continue. If any individual value falls out- side the range given, system performance is unacceptable for that compound.

NOTE: The large number of compounds in Table 5 present  a  substantial  probability that one or more will fail the acceptance cri- teria when all compounds are analyzed. To determine if the analytical system is out of control, or if the  failure  may  be  attributed to probability, proceed as follows:

      - Analyze a  second aliquot  of the aqueous performance standard  (Section 6.7.2).

      - Compute the concentration  for only those compounds which failed the first test (Section 11.5.1). If these compounds now pass, system performance is acceptable  for all compounds and analyses of blanks and samples may proceed. If, however, any of the compounds fail again, the measurement sys- tem is not performing properly for these compounds. In this event, locate and correct the problem or recalibrate the system (Sec- tion 7), and repeat the entire test (Section 11.1) for all compounds.

11.5.2 Add results which pass the speci- fication in 11.5.1.2 to initial (Section 8.2) and previous on-going data. Update QC charts to form a graphic representation of laboratory performance (Figure 7). Develop a statement of accuracy for each pollutant and labeled compound by calculating the average per- centage recovery (R) and the standard devi- ation of percent recovery (sr). Express the ac- curacy as a  recovery  interval  from  R¥2sr  to R + 2sr. For example, if R = 95% and sr  = 5%, the accuracy is 85–105 percent.

#### 40 CFR Ch. I (7–1–17 Edition)

- Qualitative Determination—Accomplished by Comparison of Data from Analysis of a Sample or Blank with Data from Analysis of the Shift Standard (Section 11.1). Identifica- tion is Confirmed When Spectra and  Reten- tion Times Agree Per the Criteria Below

  - Labeled compounds and pollutants having no labeled analog:

    - The signals for all characteristic masses stored in the spectral library (Sec- tion 7.2.4) shall be present and shall maxi- mize within the same two consecutive scans.

    - Either (1) the background corrected EICP areas, or (2) the corrected relative in- tensities of the mass spectral  peaks  at  the GC peak maximum shall agree within  a  fac- tor of two (0.5 to 2 times) for all masses stored in the library.

    - The retention time relative to the nearest eluted internal standard shall be within 7 scans or 20 seconds, whichever is greater.

  - Pollutants having a labeled analog:

    - The signals for all characteristic masses stored in the spectral library (Sec- tion 7.2.4) shall be present and shall maxi- mize within the same two consecutive scans.

    - Either (1) the background corrected EICP areas, or (2) the corrected relative in- tensities of the mass spectral  peaks  at  the GC peak maximum shall agree within  a  fac- tor of two for all masses stored in the spec- tral  library.

    - The retention time difference be- tween the pollutant and its labeled analog shall agree within 2 scans or 6 seconds (whichever is greater) of this difference  in the shift standard (Section 11.1).

12.3 Masses present in the experimental mass spectrum that are not present in the reference mass spectrum shall be accounted for by contaminant or background ions.  If the experimental mass spectrum is contami- nated, an experienced spectrometrist (Sec- tion 1.4) is to determine the presence or ab- sence of the compound.

- Quantitative Determination

  - Isotope dilution—by adding a known amount of a labeled compound to every sam- ple prior to purging, correction for recovery of the pollutant can be made because the pol- lutant and its labeled  analog  exhibit  the same effects upon purging, desorption, and gas chromatography. Relative response (RR) values for sample mixtures are used in con- junction with calibration curves described in Section 7.4 to determine concentrations di- rectly, so long as labeled compound spiking levels are constant. For the toluene example given in Figure 6 (Section 7.4.3), RR would be equal to 1.174. For this RR value, the toluene calibration curve given in Figure 5 indicates a concentration of 31.8 g/L.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1624

  - Internal standard—calculate the con- centration using the response factor deter- mined from  calibration  data  (Section  7.5) and the following equation:

Concentration  =  (As   Cis)/(Ais   RF)  where

the terms are as defined in Section 7.5.1.

  - If the EICP area at the quantitation mass for any compound exceeds the calibra- tion range of the system, the sample is di- luted by successive factors of 10 and these di- lutions are analyzed until the area is within the  calibration  range.

  - Report results for all pollutants and labeled compounds (Table 1) found in all standards, blanks, and samples, in g/L to three significant figures. Results for samples which have been diluted are reported at the least dilute level at which the area at the quantitation mass is within the calibration range (Section 13.3) and the labeled com- pound recovery is within the normal  range for the Method (Section 14.2).

- Analysis of Complex Samples

  - Untreated effluents and other  sam- ples frequently contain high levels (>1000 g/

L) of the compounds of interest and of inter- fering compounds. Some samples will foam excessively when purged; others will over- load the trap/or GC column.

  - Dilute 0.5 mL of sample with 4.5 mL of reagent water and analyze this diluted sample when labeled compound recovery is outside the range given in Table 5. If the re- covery remains outside of the range for this diluted sample, the aqueous performance standard shall be analyzed (Section 11) and calibration verified (Section 11.5). If the re- covery for the labeled compmund in the aqueous performance standard is outside the range given in Table 5, the analytical system is out of control. In this case, the instrumelt shall be repaired, the performance specifica- tions in Section 11 shall be met, and the analysis of the undiluted sample shall be re- peated. If the recovery for the aqueous per- formance standard is within the range given in Table 5, the method does not work on the sample being analyzed and the result  may not be reported for regulatory compliance purposes.

  - Reverse search computer programs can misinterpret the spectrum of chromatographically unresolved pollutant and labeled compound pairs with overlapping spectra when a high level of the pollutant is present.  Examine  each  chromatogram  for

peaks greater than the height of the internal standard peaks. These peaks can obscure the compounds of interest.

- Method Performance

15.1 The specifications for this  method were taken from the inter-laboratory valida- tion of EPA Method 624 (reference 9). Method 1624 has been shown to yield slightly better performance on treated effluents than Meth- od 624. Additional method performance data can be found in Reference 10.

References

- ‘‘Performance Tests for the  Evaluation of Computerized Gas Chromatography/Mass Spectrometry Equipment and Laboratories,’’ USEPA, EMSL/Cincinnati, OH 45268, EPA– 600/4–80–025 (April 1980).

- Bellar, T.A. and Lichtenberg, J.J., ‘‘Journal American Water Works Associa- tion,’’ 66, 739 (1974).

- Bellar, T.A. and Lichtenberg, J.J., ‘‘Semi-automated Headspace Analysis of Drinking Waters and Industrial Waters for Purgeable Volatile Organic Compounds,’’ in Measurement of Organic Pollutants Water and Wastewater, C.E. VanHall, ed., American So- ciety  for   Testing   Materials,   Philadelphia, PA, Special Technical Publication 686, (1978).

- ‘‘Working  with  Carcinogens,’’   DHEW, PHS, NIOSH, Publication 77–206 (1977).

- ‘‘OSHA Safety and Health Standards, General Industry,’’ 29 CFR part 1910, OSHA 2206, (1976).

- ‘‘Safety in Academic Chemistry Labora- tories,’’ American Chemical Society Publica- tion, Committee on Chemical Safety (1979).

- ‘‘Handbook  of  Analytical   Quality   Con- trol in Water and Wastewater Laboratories,’’ USEPA, EMSL/Cincinnati, OH 45268, EPA–4– 79–019 (March 1979).

- ‘‘Methods 330.4 and 330.5 for Total Resid- ual Chlorine,’’ USEPA, EMSL/Cincinnati, OH 45268, EPA–4–79–020 (March 1979).

- ‘‘EPA Method Study 29 EPA Method 624—Purgeables,’’ EPA 600/4–84–054, National Technical Information Service, PB84–209915, Springfield, Virginia 22161, June 1984.

- ‘‘Colby, B.N., Beimer, R.G., Rushneck, D.R., and Telliard, W.A., ‘‘Isotope Dilution Gas Chromatography-Mass Spectrometry for the Determination of Priority Pollutants in Industrial Effluents,’’ USEPA, Effluent Guidelines Division, Washington, DC 20460 (1980).

TABLE 1—VOLATILE ORGANIC COMPOUNDS ANALYZED BY ISOTOPE DILUTION GC/MS

| Compound | Storet | CAS reg- istry | EPA- EGD | NPDES |
| --- | --- | --- | --- | --- |
| Acetone ................................................................................................................... | 81552 | 67–64–1 | 516 V | 001 V |
| Acrolein ................................................................................................................... | 34210 | 107–02–8 | 002 V |  |
| Acrylonitrile .............................................................................................................. | 34215 | 107–13–1 | 003 V | 002 V |
| Benzene .................................................................................................................. | 34030 | 71–43–2 | 004 V | 003 V |
| Bromodichloromethane ........................................................................................... | 32101 | 75–27–4 | 048 V | 012 V |

#### Pt. 136, App. A, Meth. 1624

40 CFR Ch. I (7–1–17 Edition)

TABLE 1—VOLATILE ORGANIC COMPOUNDS ANALYZED BY ISOTOPE DILUTION GC/MS—Continued

| Compound | Storet | CAS reg- istry | EPA- EGD | NPDES |
| --- | --- | --- | --- | --- |
| Bromoform ............................................................................................................... | 32104 | 75–25–2 | 047 V | 005 V |
| Bromomethane ........................................................................................................ | 34413 | 74–83–9 | 046 V | 020 V |
| Carbon tetrachloride ................................................................................................ | 32102 | 56–23–5 | 006 V | 006 V |
| Chlorobenzene ........................................................................................................ | 34301 | 108–90–7 | 007 V | 007 V |
| Chloroethane ........................................................................................................... | 34311 | 75–00–3 | 016 V | 009 V |
| 2-chloroethylvinyl ether ........................................................................................... | 34576 | 110–75–8 | 019 V | 010 V |
| Chloroform ............................................................................................................... | 32106 | 67–66–1 | 023 V | 011 V |
| Chloromethane ........................................................................................................ | 34418 | 74–87–3 | 045 V | 021 V |
| Dibromochloromethane ........................................................................................... | 32105 | 124–48–1 | 051 V | 008 V |
| 1,1-dichloroethane ................................................................................................... | 34496 | 75–34–3 | 013 V | 014 V |
| 1,2-dichloroethane ................................................................................................... | 34536 | 107–06–2 | 010 V | 015 V |
| 1,1-dichloroethene ................................................................................................... | 34501 | 75–35–4 | 029 V | 016 V |
| Trans-1,2-dichloroethane ........................................................................................ | 34546 | 156–60–5 | 030 V | 026 V |
| 1,2-dichloropropane ................................................................................................ | 34541 | 78–87–5 | 032 V | 017 V |
| Cis-1,3-dichloropropene .......................................................................................... | 34704 | 10061–01–5 |  |  |
| Trans-1,3-dichloropropene ...................................................................................... | 34699 | 10061–02–6 | 033 V |  |
| Diethyl ether ............................................................................................................ | 81576 | 60–29–7 | 515 V |  |
| P-dioxane ................................................................................................................ | 81582 | 123–91–1 | 527 V |  |
| Ethylbenzene ........................................................................................................... | 34371 | 100–41–4 | 038 V | 019 V |
| Methylene chloride .................................................................................................. | 34423 | 75–09–2 | 044 V | 022 V |
| Methyl ethyl ketone ................................................................................................. | 81595 | 78–93–3 | 514 V |  |
| 1,1,2,2-tetrachloroethane ........................................................................................ | 34516 | 79–34–5 | 015 V | 023 V |
| Tetrachlorethene ..................................................................................................... | 34475 | 127–18–4 | 085 V | 024 V |
| Toluene ................................................................................................................... | 34010 | 108–88–3 | 086 V | 025 V |
| 1,1,1-trichloroethane ............................................................................................... | 34506 | 71–55–6 | 011 V | 027 V |
| 1,1,2-trichloroethane ............................................................................................... | 34511 | 79–00–5 | 014 V | 028 V |
| Trichloroethene ....................................................................................................... | 39180 | 79–01–6 | 087 V | 029 V |
| Vinyl chloride ........................................................................................................... | 39175 | 75–01–4 | 088 V | 031 V |

TABLE 2—GAS CHROMATOGRAPHY OF PURGEABLE  ORGANIC  COMPOUNDS  BY  ISO- TOPE DILUTION GC/MS

TABLE 2—GAS CHROMATOGRAPHY OF

PURGEABLE  ORGANIC  COMPOUNDS  BY  ISO-

TOPE DILUTION GC/MS—Continued

| EGD No. (1) | Compound | Ref EGD No. | Mean re- ten- tion time (sec) | Min- i mum level (2) (g/ L) |
| --- | --- | --- | --- | --- |
| 181 | Bromochloromethane (I.S.) ...... | 181 | 730 | 10 |
| 245 | Chloromethane-d3 .................... | 181 | 147 | 50 |
| 345 | Chloromethane ......................... | 245 | 148 | 50 |
| 246 | Bromomethane-d3 .................... | 181 | 243 | 50 |
| 346 | Bromomethane ......................... | 246 | 246 | 50 |
| 288 | Vinyl chloride-d3 ....................... | 181 | 301 | 50 |
| 388 | Vinyl chloride ............................ | 288 | 304 | 10 |
| 216 | Chloroethane-d5 ....................... | 181 | 378 | 50 |
| 316 | Chloroethane ............................ | 216 | 386 | 50 |
| 244 | Methylene chloride-d2 .............. | 181 | 512 | 10 |
| 344 | Methylene chloride ................... | 244 | 517 | 10 |
| 616 | Acetone-d6 ............................... | 181 | 554 | 50 |
| 716 | Acetone ..................................... | 616 | 565 | 50 |
| 002 | Acrolein ..................................... | 181 | 566 | 50 |
| 203 | Acrylonitrile-d3 .......................... | 181 | 606 | 50 |
| 303 | Acrylonitrile ............................... | 203 | 612 | 50 |
| 229 | 1,1-dichloroethene-d2 ............... | 181 | 696 | 10 |
| 329 | 1,1-dichloroethene .................... | 229 | 696 | 10 |
| 213 | 1,1-dichloroethane-d3 ............... | 181 | 778 | 10 |
| 313 | 1,1-dichloroethane .................... | 213 | 786 | 10 |
| 615 | Diethyl ether-d10 ...................... | 181 | 804 | 50 |
| 715 | Diethyl ether ............................. | 615 | 820 | 50 |
| 230 | Trans-1,2-dichloroethene-d2 .... | 181 | 821 | 10 |
| 330 | Trans-1,2-dichloroethene .......... | 230 | 821 | 10 |
| 614 | Methyl ethyl ketone-d3 ............. | 181 | 840 | 50 |
| 714 | Methyl ethyl ketone .................. | 614 | 848 | 50 |
| 223 | Chloroform-13C1 ...................... | 181 | 861 | 10 |
| 323 | Chloroform ................................ | 223 | 861 | 10 |
| 210 | 1,2-dichloroethane-d4 ............... | 181 | 901 | 10 |
| 310 | 1,2-dichloroethane .................... | 210 | 910 | 10 |
| EGD No. (1) | Compound | Ref EGD No. | Mean re- ten- tion time (sec) | Min- i mum level (2) (g/ L) |
| 211 | 1,1,1-trichloroethane-13C2 ....... | 181 | 989 | 10 |
| 311 | 1,1,1-trichloroethane ................. | 211 | 999 | 10 |
| 527 | p-dioxane .................................. | 181 | 1001 | 10 |
| 206 | Carbon tetrachloride-13C1 ....... | 182 | 1018 | 10 |
| 306 | Carbon tetrachloride ................. | 206 | 1018 | 10 |
| 248 | Bromodichloromethane-13C1 ... | 182 | 1045 | 10 |
| 348 | Bromodichloromethane ............. | 248 | 1045 | 10 |
| 232 | 1,2-dichloropropane-d6 ............. | 182 | 1123 | 10 |
| 332 | 1.2-dichloropropane .................. | 232 | 1134 | 10 |
| 233 | Trans-1,3-dichloropropene-d4 .. | 182 | 1138 | 10 |
| 333 | Trans-1,3-dichloropropene ....... | 233 | 1138 | 10 |
| 287 | Trichloroethene-13C1 ............... | 182 | 1172 | 10 |
| 387 | Trichloroethene ......................... | 287 | 1187 | 10 |
| 204 | Benzene-d6 .............................. | 182 | 1200 | 10 |
| 304 | Benzene .................................... | 204 | 1212 | 10 |
| 251 | Chlorodibromemethane-13C1 .. | 182 | 1222 | 10 |
| 351 | Chlorodibromomethane ............ | 251 | 1222 | 10 |
| 214 | 1,1,2-trichloroethane-13C2 ....... | 182 | 1224 | 10 |
| 314 | 1,1,2-trichloroethane ................. | 214 | 1224 | 10 |
| 019 | 2-chloroethylvinyl ether ............. | 182 | 1278 | 10 |
| 182 | 2-bromo-1-chloropropane (I.S.) | 182 | 1306 | 10 |
| 247 | Bromoform-13C1 ...................... | 182 | 1386 | 10 |
| 347 | Bromoform ................................ | 247 | 1386 | 10 |
| 215 | 1,1,2,2-tetrachloroethane-d2 .... | 183 | 1525 | 10 |
| 315 | 1,1,2,2-tetrachloroethane .......... | 215 | 1525 | 10 |
| 285 | Tetrachloroethene-13C2 ........... | 183 | 1528 | 10 |
| 385 | Tetrachloroethene ..................... | 285 | 1528 | 10 |
| 183 | 1,4-dichlorobutale (int std) ........ | 183 | 1555 | 10 |
| 286 | Toluene-d8 ................................ | 183 | 1603 | 10 |
| 386 | Toluene ..................................... | 286 | 1619 | 10 |

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1624

TABLE 2—GAS CHROMATOGRAPHY OF

PURGEABLE  ORGANIC  COMPOUNDS  BY  ISO-

TOPE DILUTION GC/MS—Continued

TABLE 4—VOLATILE ORGANIC COMPOUND CHARACTERISTIC MASSES

| EGD No. (1) | Compound | Ref EGD No. | Mean re- ten- tion time (sec) | Min- i mum level (2) (g/ L) |
| --- | --- | --- | --- | --- |
| 207 | Chlorobenzene-d5 .................... | 183 | 1679 | 10 |
| 307 | Chlorobenzene ......................... | 207 | 1679 | 10 |
| 238 | Ethylbenzene-d10 ..................... | 183 | 1802 | 10 |
| 338 | Ethylbenzene ............................ | 238 | 1820 | 10 |
| 185 | Bromofluorobenzene ................ | 183 | 1985 | 10 |
| Labeled compound | Analog | Primary m/ z’s |
| Acetone ............................................... | d6 | 58/64 |
| Acrolein ................................................ | d2 | 56/58 |
| Acrylonitrile .......................................... | d3 | 53/56 |
| Benzene .............................................. | d6 | 78/84 |
| Bromodichloromethane ....................... | 13C | 83/86 |
| Bromoform ........................................... | 13C | 173/176 |
| Bromomethale ..................................... | d3 | 96/99 |
| Carbon tetrachloride ............................ | 13C | 47/48 |
| Chlorobenzene .................................... | d5 | 112/117 |
| Chloroethane ....................................... | d5 | 64/71 |
| 2-chloroethylvinyl ether ....................... | d7 | 106/113 |
| Chloroform ........................................... | 13C | 85/86 |
| Chloromethane .................................... | d3 | 50/53 |
| Dibromochloromethane ....................... | 13C | 129/130 |
| 1,1-dichloroethane ............................... | d3 | 63/66 |
| 1,2-dichloroethane ............................... | d4 | 62/67 |
| 1,1-dichloroethene ............................... | d2 | 61/65 |
| Trans-1,2-dichloroethene ..................... | d2 | 61/65 |
| 1,2-dichloropropane ............................. | d6 | 63/67 |
| Cis-1,3-dichloropropene ...................... | d4 | 75/79 |
| Trans-1,3-dichloropropene .................. | d4 | 75/79 |
| Diethyl ether ........................................ | d10 | 74/84 |
| p-dioxane ............................................. | d8 | 88/96 |
| Ethylbenzene ....................................... | d10 | 106/116 |
| Methylene chloride .............................. | d2 | 84/88 |
| Methyl ethyl ketone ............................. | d3 | 72/75 |
| 1,1,2,2-tetrachloroethane ..................... | d2 | 83/84 |
| Tetrachloroethene ............................... | 13C2 | 166/172 |
| Toluene ................................................ | d8 | 92/99 |
| 1,1,1-trichloroethane ............................ | d3 | 97/102 |
| 1,1,2-trichloroethane ............................ | 13C2 | 83/84 |
| Trichloroethene .................................... | 13C | 95/133 |
| Vinyl chloride ....................................... | d3 | 62/65 |

Reference numbers beginning with 0, 1 or 5 indicate a pollutant quantified by the internal standard method; reference numbers beginning with 2 or 6 indicate a labeled compound quantified by the internal standard method; reference numbers beginning with 3 or 7 indicate a pollutant quantified by isotope dilution.

- This is a minimum level at which the analytical system shall give recognizable mass spectra (background corrected) and acceptable calibration points. Column: 2.4m (8 ft) 2 mm

i.d. glass, packed with one percent SP–1000 coated on 60/80 Carbopak B. Carrier gas: helium at 40 mL/min. Temperature program: 3 min at 45 C, 8 C per min to 240 C, hold at 240

C for 15 minutes.

NOTE: The specifications in this table were developed from data collected from three wastewater laboratories.

TABLE 3—BFB MASS-INTENSITY SPECIFICATIONS

| Mass | Intensity required |
| --- | --- |
| 50 | 15 to 40 percent of mass 95. |
| 75 | 30 to 60 percent of mass 95. |
| 95 | base peak, 100 percent. |
| 96 | 5 to 9 percent of mass 95. |
| 173 | <2 percent of mass 174. |
| 174 | >50 percent of mass 95. |
| 175 | 5 to 9 percent of mass 174 |
| 176 | 95 to 101 percent of mass 174 |
| 177 | 5 to 9 percent of mass 176. |

TABLE 5—ACCEPTANCE CRITERIA FOR PERFORMANCE TESTS

Acceptance criteria at 20 g/L

| Compound Initial precision and accuracy section 8.2.3 | Labeled compound recovery sec. 8.3 and 14.2 | On-going accuracy sec. 11.5 |
| --- | --- | --- |
|  | s (g/L) | X¯ (g/L) | P (percent) |  | R (g/L) |
| Acetone .............................................................................................. |  | Note | 1 |  |  |
| Acrolein .............................................................................................. |  | Note | 2 |  |  |
| Acrylonitrile ......................................................................................... |  | Note | 2 |  |  |
| Benzene ............................................................................................. | 9.0 | 13.0–28.2 | ns–196 |  | 4–33 |
| Bromodichloromethane ...................................................................... | 8.2 | 6.5–31.5 | ns–199 |  | 4–34 |
| Bromoform ......................................................................................... | 7.0 | 7.4–35.1 | ns–214 |  | 6–36 |
| Bromomethane ................................................................................... | 25.0 | d–54.3 | ns–414 |  | d–61 |
| Carbon tetrachloride .......................................................................... | 6.9 | 15.9–24.8 | 42–165 |  | 12–30 |
| Chlorobenzene ................................................................................... | 8.2 | 14.2–29.6 | ns–205 |  | 4–35 |
| Chloroethane ...................................................................................... | 14.8 | 2.1–46.7 | ns–308 |  | d–51 |
| 2–chloroethylvinyl ether ..................................................................... | 36.0 | d–69.8 | ns–554 |  | d–79 |
| Chloroform ......................................................................................... | 7.9 | 11.6–26.3 | 18–172 |  | 8–30 |
| Chloromethane ................................................................................... | 26.0 | d–55.5 | ns–410 |  | d–64 |
| Dibromochloromethane ...................................................................... | 7.9 | 11.2–29.1 | 16–185 |  | 8–32 |
| 1,1-dichloroethane ............................................................................. | 6.7 | 11.4–31.4 | 23–191 |  | 9–33 |
| 1,2-dichloroethane ............................................................................. | 7.7 | 11.6–30.1 | 12–192 |  | 8–33 |
| 1,1-dichloroethene ............................................................................. | 11.7 | d–49.8 | ns–315 |  | d–52 |
| Trans-1,2–dichloroethene .................................................................. | 7.4 | 10.5–31.5 | 15–195 |  | 8–34 |

#### Pt. 136, App. A, Meth. 1624

40 CFR Ch. I (7–1–17 Edition)

TABLE 5—ACCEPTANCE CRITERIA FOR PERFORMANCE TESTS—Continued

Acceptance criteria at 20 g/L

| Compound Initial precision and accuracy section 8.2.3 | Labeled compound recovery sec. 8.3 and 14.2 | On-going accuracy sec. 11.5 |
| --- | --- | --- |
|  | s (g/L) | X¯ (g/L) | P (percent) |  | R (g/L) |
| 1,2-dichloropropane ........................................................................... | 19.2 | d–46.8 | ns–343 |  | d–51 |
| Cis–1,3–dichloropropene ................................................................... | 22.1 | d–51.0 | ns–381 |  | d–56 |
| Trans–1,3–dichloropropene ............................................................... | 14.5 | d–40.2 | ns–284 |  | d–44 |
| Diethyl ether ....................................................................................... |  | Note 1 |  |  |  |
| P-dioxane ........................................................................................... |  | Note 1 |  |  |  |
| Ethyl benzene .................................................................................... | 9.6 | 15.6–28.5 | ns–203 |  | 5–35 |
| Methylene chloride ............................................................................. | 9.7 | d–49.8 | ns–316 |  | d–50 |
| Methyl ethyl ketone ............................................................................ |  | Note 1 |  |  |  |
| 1,1,2,2-tetrachloroethane ................................................................... | 9.6 | 10.7–30.0 | 5–199 |  | 7–34 |
| Tetrachloroethene .............................................................................. | 6.6 | 15.1–28.5 | 31–181 |  | 11–32 |
| Toluene .............................................................................................. | 6.3 | 14.5–28.7 | 4–193 |  | 6–33 |
| 1,1,1-trichloroethane .......................................................................... | 5.9 | 10.5–33.4 | 12–200 |  | 8–35 |
| 1,1,2-trichloroethane .......................................................................... | 7.1 | 11.8–29.7 | 21–184 |  | 9–32 |
| Trichloroethene .................................................................................. | 8.9 | 16.6–29.5 | 35–196 |  | 12–34 |
| Vinyl chloride ...................................................................................... | 27.9 | d–58.5 | ns–452 |  | d–65 |

d = detected; result must be greater than zero.

ns = no specification; limit would be below detection limit.

Note 1: Specifications not available for these compounds at time of release of this method.

Note 2: Specifications not developed for these compounds; use method 603.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1624

Pt. 136, App. A, Meth. 1625

40 CFR Ch. I (7–1–17 Edition)

METHOD 1625 REVISION B—SEMIVOLATILE OR- GANIC COMPOUNDS BY ISOTOPE DILUTION GC/ MS

- Scope and Application

  - This method is designed to determine the semivolatile toxic organic pollutants as- sociated  with  the  1976  Consent  Decree  and

additional compounds amenable to extrac- tion and analysis by capillary column gas chromatography-mass spectrometry (GC/ MS).

  - The chemical compounds listed in Ta- bles 1 and 2 may be determined in municipal and industrial discharges  by  this  method. The  method  is  designed  to  meet  the  survey

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1625

requirements of Effluent Guidelines Division (EGD) and the  National  Pollutants  Dis- charge Elimination  System (NPDES)  under 40 CFR 136.1. Any modifications of this meth- od, beyond those expressly permitted,  shall be considered as major modifications subject to application and approval of alternate test procedures under 40 CFR 136.4 and 136.5.

  - The detection limit of this method is usually dependent on the level of inter- ferences rather than instrumental limita- tions. The limits listed in Tables 3 and 4 rep- resent the minimum quantity that can be de- tected with no interferences present.

  - The GC/MS portions of this method are for use only by analysts experienced with GC/MS or under the close supervision of such qualified persons. Laboratories unfamiliar with analyses of environmental samples by GC/MS should run the performance tests in reference 1 before beginning.

- Summary of Method

  - Stable isotopically labeled analogs of the compounds of interest are added to a one liter wastewater sample. The sample is ex- tracted at pH 12–13, then at pH <2 with meth- ylene chloride using continuous extraction techniques. The extract is dried over sodium sulfate and concentrated to a volume of one mL. An internal standard is added to the ex- tract, and the extract is injected into the gas chromatograph (GC). The compounds are separated by GC and detected by a mass spectrometer (MS). The labeled compounds serve to correct the variability of the analyt- ical  technique.

  - Identification of a compound (quali- tative analysis) is performed by comparing the GC retention time and background cor- rected characteristic spectral masses with those of authentic standards.

  - Quantitative analysis is performed by GC/MS using extracted ion current profile (EICP) areas. Isotope dilution is used when labeled compounds are available; otherwise, an internal standard method is used.

  - Quality is assured through reproduc- ible calibration and testing of the extraction and GC/MS systems.

- Contamination and Interferences

  - Solvents,  reagents,   glassware,   and other sample processing hardware may yield artifacts and/or elevated baselines causing misinterpretation of chromatograms and spectra. All materials  shall  be  demonstrated to be free from interferences under the con- ditions of analysis by running method blanks initially and with each sample lot (samples started through the extraction process on a given 8 hr shift, to a maximum of  20).  Spe- cific selection of reagents and purification of solvents by distillation  in  all-glass  systems may  be  required.  Glassware  and,  where  pos-

sible, reagents are cleaned by solvent rinse and baking at 450 C for one hour minimum.

  - Interferences coextracted from sam- ples will vary considerably from source to source, depending on the diversity of the in- dustrial complex or municipality being sam- ples.

- Safety

  - The toxicity or carcinogenicity of each compound or reagent used in this meth- od has not been precisely determined; how- ever, each chemical compound should be treated as a potential health hazard. Expo- sure to these compounds should be reduced to the lowest possible level. The laboratory is responsible for maintaining a current awareness file of OSHA regulations regard- ing the safe handling of the chemicals speci- fied in this method. A reference file of data handling sheets should also be made avail- able to all personnel involved in these anal- yses. Additional information on laboratory safety can be found in references 2–4.

  - The following compounds covered by this method have been  tentatively  classified as known or suspected human or mammalian carcinogens: benzidine benzo(a)anthracene, 3,3-dichlorobenzidine,	benzo(a)pyrene, dibenzo(a,h)anthracene,		N- nitrosodimethylamine, and b-naphtylamine. Primary standards of these compounds shall be prepared in a hood, and a NIOSH/MESA approved toxic gas respirator should be worn when high concentrations are handled.

- Apparatus and Materials

  - Sampling equipment for discrete or composite  sampling.

    - Sample bottle, amber glass, 1.1 liters minimum. If amber bottles are not available, samples  shall  be  protected  from  light.  Bot- tles are detergent  water  washed,  then  sol- vent rinsed or baked at 450 C for one hour minimum  before  use.

    - Bottle caps—threaded to fit sample bottles. Caps are lined with Teflon. Alu- minum foil may be substituted if the sample is not corrosive. Liners are detergent water washed, then reagent water (Section 6.5) and solvent rinsed, and baked at approximately 200 C for one hour minimum before use.

    - Compositing  equipment—automatic or manual compositing system incorporating glass containers for collection of a minimum

1.1 liters.  Sample  containers  are  kept  at  0  to 4 C during sampling. Glass or Teflon tubing only shall be used. If the sampler uses a peri- staltic pump, a minimum length of com- pressible silicone rubber tubing  may  be  used in the pump only. Before use, the tubing is thoroughly  rinsed  with  methanol,  followed by repeated rinsings with reagent water (Section 6.5) to minimize sample contamina- tion. An integrating flow meter is  used  to collect  proportional  composite  samples.

#### Pt. 136, App. A, Meth. 1625

  - Continuous liquid-liquid extractor— Teflon or glass conncecting joints and stop- cocks without lubrication (Hershberg-Wolf Extractor) one liter capacity, Ace Glass 6841– 10, or equivalent.

  - Drying column—15 to 20 mm i.d. Pyrex chromatographic column equipped with coarse glass frit or glass wool plug.

  - Kuderna-Danish (K-D) apparatus

    - Concentrator tube—10mL, graduated (Kontes K–570050–1025, or equivalent) with calibration verified. Ground glass stopper (size 19/22 joint) is used to prevent evapo- ration  of  extracts.

    - Evaporation flask—500 mL (Kontes K–570001–0500, or equivalent), attached to concentrator tube with springs (Kontes K– 662750–0012).

    - Snyder column—three ball macro (Kontes K–503000–0232, or equivalent).

    - Snyder column—two ball  micro (Kontes K–469002–0219, or equivalent).

    - Boiling chips—approx 10/40 mesh, ex- tracted  with  methylene  chloride   and   baked at 450 C for one hr minimum.

  - Water bath—heated, with concentric ring cover, capable of temperature control 2

C, installed in a fume hood.

  - Sample vials—amber glass, 2–5 mL with Teflon-lined screw cap.

  - Analytical balance—capable of weigh- ing 0.1 mg.

  - Gas chromatograph—shall  have splitless or on-column injection port for cap- illary column, temperature program with 30

C hold, and shall meet all of the perform- ance specifications in Section 12.

5.8.1 Column—30 5 m 0.25 0.02 mm i.d. 5% phenyl, 94% methyl, 1% vinyl silicone bonded  phase  fused  silica  capillary  column  (J

& W DB–5, or equivalent).

  - Mass spectrometer—70 eV electron im- pact ionization, shall repetitively scan  from 35 to 450 amu in 0.95 to 1.00 second, and shall produce a unit resolution (valleys between m/z 441–442 less than 10 percent of the height of the 441 peak), backgound corrected mass spectrum	from	50	ng decafluorotriphenylphosphine (DFTPP) in- troduced through the GC inlet. The spectrum shall meet the mass-intensity criteria in Table 5 (reference 5). The mass spectrometer shall be interfaced to the GC such  that  the end of the capillary column terminates with- in one centimeter of the ion source but does not intercept the electron or ion beams. All portions of the column which connect the GC to the ion source shall remain  at  or  above the column temperature during analysis to preclude condensation of less volatile com- pounds.

  - Data system—shall collect and record MS data, store mass-intensity data in spec- tral libraries, process GC/MS data, generate reports, and shall compute and record re- sponse factors.

#### 40 CFR Ch. I (7–1–17 Edition)

    - Data  acquisition—mass  spectra shall be collected continuously throughout the analysis and stored on a mass storage de- vice.

    - Mass spectral libraries—user cre- ated libraries containing mass spectra ob- tained from analysis of authentic standards shall be employed to reverse search GC/MS runs for the compounds of interest (Section 7.2).

    - Data processing—the data system shall be used to search, locate, identify, and quantify the compounds of interest in each GC/MS analysis. Software routines shall be employed to compute retention times and peak areas. Displays of spectra, mass chromatograms, and library comparisons are required to verify results.

    - Response factors and multipoint calibrations—the data system shall  be  used to record and maintain lists of response fac- tors (response ratios for isotope dilution) and multipoint calibration curves (Section 7). Computations of relative standard deviation (coefficient of variation) are useful for  test- ing  calibration  linearity.  Statistics  on  ini- tial (Section 8.2) and on-going (Section 12.7) performance shall be computed and main- tained.

- Reagents and Standards

  - Sodium hydroxide—reagent grade, 6N in reagent water.

  - Sulfuric acid—reagent grade, 6N in re- agent water.

  - Sodium sulfate—reagent grade, granu- lar anhydrous, rinsed with methylene chlo- ride (20 mL/g) and conditioned at 450 C for one hour minimum.

  - Methylene chloride—distilled in glass (Burdick and Jackson, or equivalent).

  - Reagent water—water in which the compounds of interest and interfering com- pounds are not detected by this method.

  - Standard solutions—purchased as so- lutions or mixtures with  certification  to their purity, concentration,  and  authen- ticity, or prepared from materials of known purity and composition.  If  compound  purity is 96 percent or greater, the weight may be used without correction to compute the con- centration of the standard. When not being used, standards are stored in the dark at ¥20 to ¥10 C in screw-capped vials with Teflon- lined lids. A mark is placed on the vial at the level of the solution so that solvent evapo- ration loss can be detected. The vials are brought to room temperature prior to use. Any precipitate is redissolved and solvent is added if solvent loss has occurred.

  - Preparation of stock solutions—pre- pare in methylene chloride, benzene, p- dioxane, or a mixture of these  solvents  per the steps below. Observe the safety pre- cautions in Section 4. The large number of labeled and unlabeled acid, base/neutral, and Appendix  C  compounds  used  for  combined

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1625

calibration (Section 7) and calibration verification	(12.5)	require	high concentratimns (approx 40 mg/mL) when in- dividual stock solutions  are  prepared,  so that dilutions of mixtures will permit cali- bration with all compounds in a single set of solutions. The working  range for  most com- pounds is 10–200 g/mL. Compounds with a re- duced MS response may be prepared at high- er  concentrations.

    - Dissolve an appropriate amount of assayed reference material in a suitable sol- vent. For example, weigh 400 mg naphthalene in a 10 mL ground glass stoppered volumetric flask and fill  to  the  mark  with  benzene. After the naphthalene is completely dis- solved, transfer the solution to a 15 mL vial with Teflon-lined cap.

    - Stock standard solutions should be checked for signs of degradation prior to the preparation of calibration or performance test standards. Quality control check sam- ples that can be used to determine the accu- racy of calibration standards are available from the US Environmental Protection Agency, Environmental Monitoring and Sup- port Laboratory, Cincinnati, Ohio 45268.

    - Stock standard solutions shall be re- placed after six months, or sooner if com- parison with quality control check samples indicates a change in concentration.

  - Labeled compound spiking solution— from stock standard solutions prepared as above, or from mixtures, prepare the spiking solution at a concentration of 200 g/mL, or at a concentration appropriate to the MS re- sponse of each compound.

  - Secondary standard—using stock solu- tions (Section 6.7), prepare a secondary standard containing all of the compounds in Tables 1 and 2 at a concentration of 400 g/ mL, or higher concentration appropriate to the MS response of the compound.

  - Internal standard solution—prepare 2,2-difluorobiphenyl (DFB) at a concentra- tion of 10 mg/mL in benzene.

  - DFTPP solution—prepare at 50 g/mL in acetone.

  - Solutions for obtaining authentic mass spectra (Section 7.2)—prepare mixtures of compounds at concentrations which will assure authentic spectra are obtained for storage in libraries.

  - Calibration   solutions—combine    0.5 mL of the solution in Section 6.8 with 25, 50, 125, 250, and 500 uL of the solution in section

6.9 and bring to 1.00 mL total volume each. This will produce calibration solutions of nominal 10, 20, 50, 100, and 200 g/mL of the pollutants and a constant nominal 100 g/mL of the labeled compounds. Spike each solu- tion with 10 L of the internal standard solu- tion (Section 6.10). These solutions permit the relative response (labeled  to  unlabeled) to be measured as a function of concentra- tion (Section 7.4).

  - Precision and recovery  standard— used for determination of initial (Section 8.2) and on-going (Section 12.7) precision and re- covery. This solution shall contain the pol- lutants and labeled compounds at a nominal concentration of 100 g/mL.

  - Stability of solutions—all standard solutions (Sections 6.8–6.14) shall be analyzed within 48 hours of preparation and on a monthly basis thereafter for signs of deg- radation. Standards  will  remain  acceptable if the peak area at the quantitation mass relative to the DFB internal standard  re- mains within 15 percent of the area ob- tained in the initial analysis of the standard.

- Calibration

  - Assemble the GC/MS and establish the operating conditions in Table 3. Analyze standards per the procedure in Section 11 to demonstrate that the analytical  system meets the detection limits in Tables 3 and 4, and the mass-intensity criteria in Table 5 for 50 ng DFTPP.

  - Mass spectral libraries—detection and identification of compounds of interest are dependent upon spectra stored in user cre- ated  libraries.

    - Obtain a mass spectrum of each pol- lutant, labeled compound, and the internal standard by analyzing an authentic standard either singly or as part of a mixture in which there is no interference between closely eluted components. That only a single com- pound is present is determined by examina- tion of the spectrum. Fragments not attrib- utable to the compound under study indicate the presence of an interfering compound.

    - Adjust the analytical conditions and scan rate (for this test only) to produce an undistorted spectrum at the GC peak max- imum. An undistorted spectrum will usually be obtained if five complete spectra are col- lected across the upper half of the GC peak. Software algorithms designed to ‘‘enhance’’ the spectrum may eliminate distortion, but may also eliminate authentic masses or in- troduce other distortion.

    - The authentic reference spectrum is obtained under DFTPP tuning conditions (Section 7.1 and Table 5) to normalize it to spectra from other instruments.

    - The spectrum is edited by saving the

5 most intense mass spectral peaks and all other mass spectral peaks greater than 10 percent of the base peak. This edited spec- trum is stored for reverse search and for compound  confirmation.

7.3 Analytical range—demonstrate that 20 ng anthracene or phenanthrene produces an area at m/z 178 approx one-tenth that re- quired to exceed the linear range of the sys- tem. The exact value must be determined by experience for each instrument. It is used to match the calibration range of the instru- ment to the analytical range and detection limits  required,  and  to  diagnose  instrument

#### Pt. 136, App. A, Meth. 1625

sensitivity problems (Section 15.4). The 20 ug/mL calibration standard (Section 6.13) can be  used  to  demonstrate  this  performance.

7.3.1 Polar compound detection—dem- onstrate that unlabeled pentachlorophenol and benzidine are detectable at the 50 g/mL level (per all criteria in  Section 13). The 50

g/mL calibration standard (Section 6.13) can be used to demonstrate this performance.

  - Calibration with isotope dilution—iso- tope dilution is used when (1) labeled com- pounds are available, (2) interferences do not preclude its use, and (3) the quantitation mass extracted ion current  profile  (EICP) area for the compound is in the calibration range. If any of these conditions preclude isotope dilution, internal standard methods (Section 7.5 or 7.6) are used.

    - A  calibration  curve   encompassing the concentration range is prepared for each compound to be determined. The relative re- sponse (pollutant to labeled) vs concentra- tion in standard solutions is plotted or com- puted using a linear regression. The example in Figure 1 shows a calibration curve for phe- nol using phenol-d5 as the isotopic diluent. Also shown are the 10 percent error limits (dotted lines). Relative Reponse (RR) is de- termined according to the procedures de- scribed below. A minimum of five  data points are employed for calibration.

    - The relative response of  a  pollutant to its labeled analog is determined from iso- tope ratio values computed from acquired data. Three isotope ratios are used in this process:

RX = the isotope ratio measured for the pure pollutant.

Ry = the isotope ratio measured for the la- beled compound.

Rm    =   the   isotope   ratio   of   an   analytical mixture of pollutant and labeled compounds.

The m/z’s are selected such that RX>Ry. If Rm is not between 2Ry and 0.5RX, the method does not apply and the sample is analyzed by internal or external standard methods.

    - Capillary columns usually  separate the pollutant-labeled pair, with the labeled compound eluted first (Figure 2). For this case, RX = [area m1/z]/1, at the retention time of the pollutant (RT2). Ry = 1/[area m2/z, at the retention time of the labeled compound RT1). Rm = [area at m1/z (at RT2)]/[area at RT1)], as measured in the mixture of the pol- lutant and labeled compounds (Figure 2), and RR = Rm.

    - Special precautions are taken when the pollutant-labeled pair is not separated, or when another labeled compound with interfering spectral masses overlaps the pol- lutant (a case which can occur with isomeric compounds). In this case, it is necessary to determine the respective contributions of the pollutant and labeled compounds to the respective EICP areas. If the peaks are sepa- rated well enough to permit the data system

#### 40 CFR Ch. I (7–1–17 Edition)

or operator to remove  the contributions  of the compounds to each  other,  the  equations in Section 7.4.3 apply. This  usually  occurs when the height of the valley between  the two GC peaks at the same m/z is less than 10 percent of the height of the shorter  of  the two peaks. If significant GC and spectral overlap occur, RR is computed using the fol- lowing   equation:

RR = (Ry  ¥ Rm) (RX  + 1)/(Rm  ¥ RX) (Ry  + 1),

where RX is measured as shown in Figure 3A, Ry is measured as shown  in  Figure  3B,  and Rm is measured as shown in Figure 3C. For example, RX = 46100/4780 = 9.644, Ry = 2650/ 43600 = 0.0608, Rm = 49200/48300 = 1.019. amd RR

= 1.114.

    - To calibrate the analytical system by isotope dilution, analyze a 1.0 L aliquot of each of the calibration standards (Section 6.13) using the procedure in Section 11. Com- pute the RR at each concentration.

    - Linearity—if the  ratio  of  relative  re- sponse to concentration for any compound is constant (less than 20 percent coefficient of variation) over the 5 point calibration range, and averaged relative response/concentration ratio may be used for that compound; other- wise, the complete calibration curve for that compound shall be used over the 5 point cali- bration range.

  - Calibration by internal standard—used when criteria for istope dilution (Section 7.4) cannot be met. The internal standard to be used for both acid and base/neutral analyses is 2,2–difluorobiphenyl. The internal stand- ard method is also applied to determination of compounds having no labeled analog, and to measurement of labeled compounds for intra-laboratory statistics (Sections 8.4 and 12.7.4).

    - Response factors—calibration re- quires the determination of response factors (RF) which are defined by the following equation:

RF = (As  Cis)/(Ais  Cs), where

As is the area of the characteristic mass for the compmund in the daily standard

Ais  is  the  area  of  the  characteristic  mass for the internal standard

Cis   is  the  concentration  of  the  internal standard (g/mL)

Cs is the concentration of the compound in the daily standard (g/mL)

      - The response  factor  is  determined for  at  least  five   concentrations   appropriate to the response of each compound (Section 6.13); nominally, 10, 20, 50, 100, and 200 g/mL. The amount of  internal  standard  added  to each extract is the same (100 g/mL) so that Cis remains constant. The RF is plotted vs concentration for each compound in the standard  (Cs)  to  produce  a  calibration  curve.

      - Linearity—if the response factor (RF) for any compound is constant (less than 35 percent coefficient of variation) over the 5

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1625

point calibration range, an averaged re- sponse factor may be used for that com- pound; otherwise, the complete calibration curve for that compound shall be used over the 5 point range.

7.6 Combined calibration—by using cali- bration solutions  (Section  6.13)  containing the pollutants, labeled compounds, and the internal  standard,  a  single  set  of  analyses can be  used to produce calibration curves  for the isotope dilution and internal standard methods. These curves are verified each shift (Section 12.5) by analyzing  the 100 g/mL calibration standard (Section 6.13). Re- calibration is required only if calibration verification (Section 12.5) criteria cannot be met.

- Quality Assurance/Quality Control

  - Each laboratory that uses this method is required to operate a formal quality assur- ance program. The minimum requirements of this program consist of an initial dem- onstration of laboratory capability, analysis of samples spiked with labeled compounds to evaluate and document data quality, and analysis of standards and blanks as tests of continued performance. Laboratory perform- ance is compared to established performance criteria to determine if the results of anal- yses meet the performance characteristics of the method.

    - The analyst shall make an initial demonstration of the ability to generate ac- ceptable accuracy and precision with this method. This ability is established as de- scribed in Section 8.2.

    - The analyst is permitted to modify this method to improve separations or lower the costs of measurements, provided all per- formance specifications are met. Each time a modification is made to the method, the ana- lyst is required to repeat the procedure in Section 8.2 to demonstrate method perform- ance.

    - Analyses of blanks are required to demonstrate freedom from contamination. The procedures and criteria for analysis of a blank are described in Section 8.5.

    - The laboratory shall spike all sam- ples with labeled compounds to monitor method performance. This test  is  described in Section 8.3. When results of these spikes indicate atypical method performance for samples, the samples are diluted to bring method performance within acceptable lim- its (Section 15).

    - The laboratory shall, on an on-going basis, demonstrate through calibration verification and the analysis of the precision and recovery standard (Section 6.14) that the analysis system is in control. These proce- dures are described in Sections 12.1, 12.5, and 12.7.

    - The laboratory shall maintain records to define the quality of data that is

generated. Development of accuracy state- ments is described in Section 8.4.

  - Initial precision and accuracy—to es- tablish the ability to generate acceptable precision and accuracy, the analyst shall perform the following operations:

    - Extract,  concentrate,  and  analyze two sets of four one-liter aliquots (8 aliquots total) of the precision and recovery standard (Section 6.14) according to the procedure in Section 10.

    - Using results of the first set of four analyses, compute the average recovery (X¯ )

in g/mL and the standard deviation of the recovery (s) in qg/L for each compound, by isotope dilution for pollutants with a labeled analog, and by internal standard for labeled compounds and pollutants with no labeled analog.

    - For each compound, compare s and X¯

with the corresponding limits for initial pre- cision and accuracy in Table 8. If s and X¯  for

all compounds meet the acceptance criteria, system performance is acceptable and anal- ysis of blanks and samples may begin. If, however, any individual s exceeds the preci-

sion limit or any individual X¯  falls outside

the range for  accuracy,  system  performance is unacceptable for that compound.

NOTE: The large number of compounds in Table 8 present  a  substantial  probability that one or more will fail the acceptance cri- teria when all compounds are analyzed. To determine if the analytical system is out of control, or if the failure can be attributed to probability, proceed as follows:

    - Using the results of the second set of four  analyses,  compute  s  and  X¯   for  only

those compounds which failed the test of the first set  of four  analyses (Section 8.2.3).  If these compounds now pass, system perform- ance is acceptable for all compounds and analysis of blanks and samples may begin. If, however, any of the same compoulds fail again, the analysis system is not performing properly for these compounds. In this event, correct the problem and repeat the entire test (Section 8.2.1).

  - The laboratory shall spike all samples with labeled compounds to assess method performance on the sample matrix.

    - Analyze each  sample  according  to the method in Section 10.

    - Compute the percent recovery (P) of the labeled compounds using the internal standard methmd (Section 7.5).

    - Compare the labeled compound re- covery for each compound with the cor- responding limits in Table 8. If the recovery of any compounds falls outside its warning limit, method performance is unacceptable for that compound in that sample, Therefore, the sample is complex and is to  be  diluted and reanalyzed per Section 15.4.

  - As part of the QA program for the lab- oratory, method accuracy for wastewater samples  shall  be  assessed  and  records  shall

#### Pt. 136, App. A, Meth. 1625

be maintained. After the analysis of five wastewater samples for which the labeled compounds pass the tests in Section 8.3, compute the average percent recovery (P) and the standard deviation of the percent re- covery (sp) for the labeled compounds only. Express the accuracy assessment as a per- cent recovery interval from P—2 sp to P + 2sp. For example, if P = 90% and sp = 10%, the ac- curacy interval is expressed as 70–100%. Up- date the accuracy assessment for each com- pound on a regular basis (e.g. after each 5–10 new accuracy measurements).

  - Blanks—reagent water blanks are ana- lyzed to demonstrate freedom from contami- nation.

    - Extract  and  concentrate  a  blank with each sample lot (samples started through the extraction  process  on  the  same 8 hr shift, to a maximum of 20 samples). Ana- lyze the blank immediately after analysis  of the precision and recovery standard (Section 6.14) to demonstrate freedom from contami- nation.

    - If any of the compounds of interest (Tables 1 and 2) or any potentially inter- fering compound is found in a blank at great- er than 10 g/L (assuming a response factor of 1 relative to the internal standard for compounds not listed in Tables 1 and 2), analysis of samples is halted until the source of contamination is eliminated and a blank shows no evidence of contamination at this level.

  - The specifications contained in this method can be met if the apparatus used is calibrated properly, then maintained in a calibrated state. The standards used for cali- bration (Section 7), calibration verification (Section 12.5), and for initial (Section 8.2) and on-going (Section 12.7) precision and re- covery should be identical, so that the most precise results will be obtained. The GC/MS instrument in particular will provide  the most reproducible results if dedicated to the settings and conditions required for the anal- ysis of semi-volatiles by this method.

  - Depending on specific program re- quirements, field replicates may be collected to determine the precision of the sampling technique, and spiked samples may be re- quired to determine the accuracy of the analysis when internal or external standard methods are used.

- Sample Collection, Preservation, and Handling

  - Collect samples in glass containers following conventional sampling practices (Reference 7). Composite samples are col- lected in refrigerated glass containers (Sec- tion 5.1.3) in accordance with the require- ments of the sampling program.

  - Maintain  samples  at  0–4  C  from  the

time collectimn until extraction. If residual chlorine is present, add 80 mg sodium thiosulfate  per  liter  of  water.  EPA  Methods

#### 40 CFR Ch. I (7–1–17 Edition)

330.4 and 330.5 may be used to measure resid- ual  chlorine  (Reference  8).

9.3 Begin sample extraction within seven days of collection, and analyze all extracts within  40  days  of  extraction.

- Sample Extraction and Concentration (See Figure 4)

  - Labeled  compound  spiking—measure

1.00 0.01 liter of sample into a glass con- tainer. For untreated effluents, and samples which are expected to be difficult to extract and/or  concentrate,  measure  an  additional

10.0 0.1 mL and dilute to a final volume of

1.00 0.01 liter with reagent water in a glass container.

    - For each sample or sample lot (to a maximum of 20) to be extracted at the same time, place three 1.00 0.10 liter aliquots of reagent  water  in  glass  containers.

    - Spike 0.5 mL of the labeled com- pound spiking solution (Section 6.8) into all samples and one reagant water aliquot.

    - Spike 1.0 mL of the precision and recovery standard (Section 6.14) into the two remaining reagent water aliquots.

    - Stir and equilibrate all solutions for 1–2 hr.

  - Base/neutral extraction—place 100–150 mL methylene chloride in each continuous extractor  and  200–300  in  each  distilling  flask.

    - Pour the sample(s), blank, and standard aliquots into the extractors. Rinse the glass containers with 50–100 mL meth- ylene chloride and add to the respective ex- tractor.

    - Adjust the pH of the waters in the extractors to 12–13 with 6N NaOH while mon- itoring  with  a  pH  meter.  Begin  the  extrac- tion by heating  the  flask  until  the  meth- ylene chloride is boiling. When properly ad- justed, 1–2 drops of methylene chloride per second will fall from the condensor  tip  into the water. After 1–2 hours of  extraction,  test the pH and readjust to  12–13 if required. Ex- tract for 18–24 hours.

    - Remove the distilling flask, esti- mate and record the volume of  extract  (to the nearest 100 mL), and pour the contents through a drying column containing 7 to 10 cm anhydrous sodium sulfate. Rinse the dis- tilling flask with 30–50 mL of methylene chloride and pour through the drying col- umn. Collect the solution in a 500 mL K-D evaporator flask equipped with a 10 mL con- centrator tube. Seal, label as the base/neu- tral fraction, and concentrate per Sections 10.4 to 10.5.

10.3 Acid extraction—adjust the pH of the waters in the extractors to 2 or less using 6N sulfuric acid. Charge clean  distilling  flasks with 300–400 mL of methylene chloride. Test and  adjust  the  pH  of  the  waters  after   the first 1–2 hr of extraction. Extract for 18–24 hours.

10.3.1 Repeat Section  10.2.3,  except  label as the acid fraction.

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1625

  - Concentration—concentrate the ex- tracts in separate 500 mL K-D flasks equipped with 10 mL concentrator tubes.

    - Add 1 to 2 clean boiling chips to the flask and attach a three-ball macro Snyder column. Prewet the column by adding ap- proximately one mL of methylene chloride through the top. Place the K-D apparatus  in a hot water bath so that the entire lower rounded surface of the flask is bathed with steam. Adjust the vertical position of the ap- paratus and the water temperature as re- quired to complete the concentration in 15 to 20 minutes. At the proper rate of distillation, the balls of the column will  actively  chatter but the chambers will not flood. When the liquid has reached an apparent volume of  1 mL, remove the K-D apparatus from the bath and allow the solvent to drain and cool for at least 10 minutes. Remove the Snyder column and rinse the flask and its  lower  joint  into the concentrator tube with 1–2 mL of meth- ylene chloride. A 5-mL syringe is rec- ommended for this operation.

    - For performance standards (Sec- tions 8.2 and 12.7) and for blanks (Section 8.5), combine the acid and base/neutral ex- tracts for each at this point. Do not combine the acid and base/neutral extracts for sam- ples.

  - Add a clean boiling chip and attach a two ball micro Snyder column to the concen- trator tube. Prewet the column by adding approx 0.5 mL methylene chloride through the top. Place the apparatus in the hot water bath. Adjust  the vertical  position  and the water temperature as required to complete the concentration in 5–10 minutes. At the proper rate of distillation, the balls of the column will actively chatter but the cham- bers will not flood. When the liquid reaches an apparent volume of approx 0.5 mL, re- move the apparatus from the water bath and allow to drain and cool for at least 10 min- utes. Remove the micro Snyder column and rinse its lower joint into the concentrator tube with approx 0.2 mL of methylene chlo- ride. Adjust the final volume to 1.0 mL.

  - Transfer the concentrated extract to a clean screw-cap vial. Seal the vial with a Teflon-lined lid, and mark the level on the vial. Label with the sample number and frac- tion, and store in the dark at ¥20 to ¥10 C until ready for analysis.

- GC/MS Analysis

  - Establish the operating conditions given in Table 3 or 4 for analysis of the base/ neutral or acid extracts, respectively. For analysis of combined  extracts  (Section 10.4.2), use the operating conditions in Table 3.

  - Bring the concentrated extract (Sec- tion 10.6) or standard (Sections 6.13 through 6.14) to room temperature and verify that any precipitate has redissolved. Verify the level  on  the  extract  (Sections  6.6  and  10.6)

and bring to the mark with solvent if re- quired.

  - Add the internal standard solution (Section 6.10) to the extract (use 1.0 uL of so- lution per 0.1 mL of extract) immediately prior to injection to minimize the possibility of loss by evaporation, adsorption, or reac- tion. Mix thoroughly.

  - Inject a volume of the standard solu- tion or extract such that 100 ng of the inter- nal standard will be injected, using on-col- umn or splitless injection. For  1  mL  ex- tracts, this volume will be  1.0  uL.  Start  the GC column initial isothermal hold upon in- jection. Start MS data collection after the solvent peak elutes. Stop  data  collection after the benzo (ghi) perylene or pentachlorophenol peak elutes for the base/ neutral or acid fraction, respectively. Return the column to the initial temperature for analysis of the next sample.

- System and Laboratory Performance

  - At the beginning of each 8 hr shift during which analyses are performed, GC/MS system performance and calibration are verified for all pollutants and labeled com- pounds.  For  these  tests,  analysis  of  the  100

g/mL calibration standard (Section 6.13) shall be used to verify all performance cri- teria. Adjustment and/or recalibration (per Section 7) shall be performed until all per- formance criteria are met. Only after all per- formance criteria are met may samples, blanks, and precision and recovery standards be analyzed.

  - DFTPP   spectrum   validity—inject   1

L of the DFTPP solution (Section 6.11) ei- ther separately or within a few seconds of in- jection of the standard  (Section  12.1)  ana- lyzed at the beginning of each shift. The cri- teria in Table 5 shall be met.

  - Retention times—the absolute reten- tion time of 2,2-difluorobiphenyl shall be within the range of 1078 to 1248 seconds and the relative retention times of all pollutants and labeled compounds shall fall within the limits given in Tables 3 and 4.

  - GC resolution—the valley height be- tween  anthracene  and  phenanthrene  at  m/z

178 (or the analogs at m/z 188) shall not  ex- ceed 10 percent of the taller of the two peaks.

  - Calibration	verification—compute the concentration of each pollutant (Tables 1 and 2) by isotope dilution (Section 7.4) for those compounds which have  labeled analogs. Compute the concentration of each pollutant which has no labeled analog by the internal standard method (Section 7.5). Com- pute the concentration of the labeled com- pounds by the internal standard method. These concentrations are computed based on the calibration data determined in Section 7.

12.5.1 For each pollutant and labeled com- pound being tested, compare the concentra- tion  with  the  calibration  verification  limit

#### Pt. 136, App. A, Meth. 1625

in Table 8. If all compounds meet the accept- ance criteria, calibration has been verified and analysis of blanks, samples, and preci- sion and recovery standards may proceed. If, however, any compound fails, the measure- ment system is not performing properly for that compound. In this event, prepare a fresh calibration standard or correct the problem causing the failure and repeat the test (Sec- tion 12.1), or recalibrate (Section 7).

  - Multiple peaks—each compound in- jected shall give a single, distinct GC peak.

  - On-going precision and accuracy.

    - Analyze the extract of one of the pair of precision and recovery standards (Section 10.1.3) prior to analysis of samples from the same lot.

    - Compute the concentration of each pollutant (Tables 1 and 2) by isotope dilution (Section 7.4) for those compounds which have labeled analogs. Compute the  concentration of each  pollutant  which  has  no  labeled ana- log by the internal standard method (Section 7.5). Compute the concentration of the la- beled compounds by the internal standard method.

    - For each pollutant and labeled com- pound, compare the concentration with the limits for on-going accuracy in Table 8. If all compounds meet the acceptance criteria, system performance is acceptable and anal- ysis of blanks and samples may proceed. If, however, any individual concentration falls outside of the range given, system perform- ance is unacceptable for that compound.

NOTE: The large number of compounds in Table 8 present  a  substantial  probability that one or more will fail when all com- pounds are analyzed. To determine if the ex- traction/concentration system is out of con- trol or if the failure is caused by probability, proceed as follows:

      - Analyze the second aliquot of the pair of precision and recovery standard (Sec- tion 10.1.3).

      - Compute  the  concentration   of only those pollutants or labeled compounds that failed the previous test (Section 12.7.3). If these compounds now pass, the extraction/ concentration processes are in control and analysis of blanks and samples may proceed. If, however, any of the same compounds fail again, the extraction/concentration proc- esses are not being performed properly for these compounds. In this event, correct the problem,  re-extract  the  sample  lot  (Section

10) and repeat the on-going precision and re- covery  test  (Section  12.7).

12.7.4 Add results which pass the speci- fications in Section 12.7.2 to initial and pre- vious on-going  data. Update  QC charts  to perform a graphic representation of contin- ued laboratory performance (Figure 5). De- velop a statement of laboratory accuracy for each pollutant and labeled compound by cal- culating the  average  percent  recovery  (R) and the standard deviation of percent recov-

#### 40 CFR Ch. I (7–1–17 Edition)

ery (sr). Express the accuracy as a recovery interval from R¥2sr to R + 2sr. For example, if R = 95% and sr = 5%, the accuracy is 85¥105%.

- Qualitative Determination

  - Qualititative determination is ac- complished by comparison of data from anal- ysis of a sample or blank with data from analysis of the shift standard (Section 12.1) and with data stored in the spectral libraries (Section 7.2.4). Identification is confirmed when spectra and retention  times agree per the criteria below.

  - Labeled compounds and pollutants having no labeled analog:

    - The signals for all characteristic masses stored in the spectral library (Sec- tion 7.2.4) shall be present and shall maxi- mize within the same two consecutive scans.

    - Either (1) the background corrected EICP areas, or (2) the corrected relative in- tensities of the mass spectral  peaks  at  the GC peak maximum shall agree within  a  fac- tor of two (0.5 to 2 times) for all masses stored in the library.

    - The retention time relative to the nearest eluted  internal  standard  shall  be within 15 scans or 15 seconds, whichever is greater of this difference in the  shift  stand- ard (Section 12.1).

13.3    Pollutants having a labled analog:

13.3.1 The signals for all characteristic masses stored in the spectral library (Sec- tion 7.2.4) shall be present and shall maxi- mize within the same two consecutive scans.

    - Either (1) the background corrected EICP areas, or (2) the corrected relative in- tensities of the mass spectral  peaks  at  the GC peak maximum shall agree within  a  fac- tor of two for all masses stored in the spec- tral  library.

    - The retention time difference be- tween the pollutant and its labeled analog shall agree within 6 scans or 6 seconds (whichever is greater) of this difference  in the shift standard (Section 12.1).

13.4 Masses present in the experimental mass spectrum that are not present in the reference mass spectrum shall be accounted for by contaminant or background ions.  If the experimental mass spectrum is contami- nated, an experienced spectrometrist (Sec- tion 1.4) is to determine the presence or ab- sence of the cmmpound.

- Quantitative Determination

  - Isotope dilution—by adding a known amount of a labeled compound to every sam- ple prior to extraction, correction for recov- ery of the pollutant can be made because the pollutant and its labeled analog exhibit the same effects upon extraction, concentration, and gas chromatography. Relative response (RR) values for mixtures are used in conjunc- tion  with  calibration  curves  described  in

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1625

Section 7.4 to determine concentrations di- rectly, so long as labeled compound spiking levels are constant. For the phenml example given in Figure 1 (Section 7.4.1), RR would be equal to 1.114. For this RR value, the phenol calibration curve given in Figure 1 indicates a concentration of 27 g/mL in the sample ex- tract  (Cex).

  - Internal standard—compute the con- centration in the extract using the response factor determined from calibration data (Section 7.5) and the following equation: Cex(g/mL) = (As Cis/(Ais RF) where Cex is the concentration of the compound in the ex- tract, and  the other  terms  are as  defined  in Section 7.5.1.

  - The concentration of the  pollutant in water is computed using the volumes of the original water sample (Section 10.1) and the final extract volume (Section 10.5), as fol- lows: Concentration in water (g/L) = (Cex  Vex)/Vs where Vex is the extract  volume  in mL, and Vs  is the sample volume in liters.

  - If the EICP area at the quantitiation mass for any compound exceeds the calibra- tion range of the system, the extract of the dilute aliquot (Section 10.1) is analyzed by isotope dilution; otherwise, the extract is di- luted by a factor of 10, 9 L of internal stand- ard solution (Section 6.10) are added to a 1.0 mL aliquot, and this diluted extract is ana- lyzed by the internal standard method (Sec- tion 14.2). Quantify each compound at the highest concentration level within the cali- bration range.

  - Report results for all pollutants and labeled compounds  (Tables 1 and  2) found in all standards, blanks, and samples in g/L, to three significant figures. Results for samples which have been diluted are reported at the least dilute level at which the area at the quantitation mass is within the calibration range (Section 14.4) and the labeled com- pound recovery is within the normal  range for the method (Section 15.4).

- Analysis of Complex Samples

  - Untreated effluents and other  sam- ples frequently contain high levels (>1000 g/

L) of the compounds of interest, interfering compounds, and/or polymeric materials. Some samples will not concentrate to  one mL (Section 10.5); others will  overload  the GC column and/or mass spectrometer.

  - Analyze the dilute aliquot (Section 10.1) when the sample will not concentrate to

1.0 mL. If a dilute aliquot was not extracted, and the sample holding time (Section 9.3) has not been exceeded, dilute an aliquot of the sample with reagent water and re-extract (Section 10.1); otherwise, dilute the extract (Section 14.4) and analyze by the internal standard method (Section 14.2).

  - Recovery of internal standard—the EICP area of the internal standard should be within a factor of two of the area in the shift standard (Section 12.1). If the absolute areas

of the labeled compounds are within a factor of two of the respective areas in the shift standard, and the internal standard area is less than one-half of its respective area, then internal standard loss in the extract has oc- curred. In this case, use one of the labeled compounds (perferably a polynuclear aro- matic hydrocarbon) to compute the con- centration of a pollutant with no labeled analog.

  - Recovery of labeled compounds—in most samples, labeled compound recoveries will be similar to those from reagent water (Section 12.7). If the labeled compound recov- ery is outside the limits given in Table 8, the dilute extract (Section 10.1) is analyzed as in Section 14.4. If the recoveries of all labeled compounds and the internal staldard are low (per the criteria above), then a loss in instru- ment sensitivity is the most likely cause.  In this case, the 100 g/mL calibration standard (Section 12.1)  shall be analyzed and calibra- tion verified (Section 12.5). If a loss in sensi- tivity has occurred, the instrument shall be repaired, the performance specifications in Section 12 shall be met, and the extract re- analyzed. If a loss in instrument  sensitivity has not occurred, the method does not work on the sample being analyzed and the result may not be reported for regulatory compli- ance purposes.

- Method Performance

  - Interlaboratory performance for this method is detailed in references 9 and 10.

  - A   chromatogram   of   the   100   g/mL

acid/base/neutral calibration standard (Sec- tion 6.13) is shown in Figure 6.

REFERENCES

- ‘‘Performance Tests for the  Evaluation of Computerized Gas Chromatography/Mass Spectrometry Equipment and Laboratories’’ USEPA, EMSL/Cincinnati, OH 45268, EPA– 600/4–80–025 (April 1980).

- ‘‘Working  with  Carcinogens,’’   DHEW, PHS, CDC, NIOSH,  Publication  77–206,  (Au- gust 1977).

- ‘‘OSHA Safety and Health Standards, General Industry’’ OSHA 2206, 29 CFR part 1910 (January 1976).

- ‘‘Safety in Academic Chemistry Labora- tories, ’’ ACS Committee on Chemical Safety (1979).

- ‘‘Reference Compound to Calibrate Ion Abundance Measurement in Gas Chroma- tography-Mass Spectrometry Systems,’’ J.W. Eichelberger, L.E. Harris, and W.L.  Budde, Anal. Chem., 47, 955 (1975).

- ‘‘Handbook of Analytical  Quality  Con- trol in Water and Wastewater Laboratories,’’ USEPA, EMSL/Cincinnati, OH 45268, EPA– 600/4–79–019 (March 1979).

- ‘‘Standard  Practice  for   Sampling Water,’’ ASTM Annual Book of Standards, ASTM, Philadelphia,  PA, 76  (1980).

#### Pt. 136, App. A, Meth. 1625

- ‘‘Methods 330.4 and 330.5 for Total Resid- ual  Chlorine,’’   USEPA,   EMSL/   Cincinnati, OH 45268, EPA 600/4–70–020 (March 1979).

- Colby, B.N., Beimer, R.G., Rushneck, D.R., and Telliard, W.A., ‘‘Isotope Dilution Gas Chromatography-Mass Spectrometry for the determination of Priority Pollutants in

#### 40 CFR Ch. I (7–1–17 Edition)

Industrial Effluents.’’ USEPA, Effluent Guidelines Division, Washington, DC 20460 (1980).

- ‘‘Inter-laboratory Validation of US En- vironmental   Protection   Agency   Method 1625,’’ USEPA, Effluent Guidelines Division, Washington, DC 20460 (June 15, 1984).

TABLE 1—BASE/NEUTRAL EXTRACTABLE COMPOUNDS

| Compound | STORET | CAS reg- istry | EPA- EGD | NPDES |
| --- | --- | --- | --- | --- |
| Acenaphthene ......................................................................................................... | 34205 | 83–32–9 | 001 B | 001 B |
| Acenaphthylene ...................................................................................................... | 34200 | 208–96–8 | 077 B | 002 B |
| Anthracene ............................................................................................................. | 34220 | 120–12–7 | 078 B | 003 B |
| Benzidine ................................................................................................................ | 39120 | 92–87–5 | 005 B | 004 B |
| Benzo(a)anthracene ............................................................................................... | 34526 | 56–55–3 | 072 B | 005 B |
| Benzo(b)fluoranthene ............................................................................................. | 34230 | 205–99–2 | 074 B | 007 B |
| Benzo(k)fluoranthene ............................................................................................. | 34242 | 207–08–9 | 075 B | 009 B |
| Benzo(a)pyrene ...................................................................................................... | 34247 | 50–32–8 | 073 B | 006 B |
| Benzo(ghi)perylene ................................................................................................. | 34521 | 191–24–2 | 079 B | 008 B |
| Biphenyl (Appendix C) ............................................................................................ | 81513 | 92–52–4 | 512 B |  |
| Bis(2-chloroethyl) ether .......................................................................................... | 34273 | 111–44–4 | 018 B | 011 B |
| Bis(2-chloroethyoxy)methane ................................................................................. | 34278 | 111–91–1 | 043 B | 010 B |
| Bis(2-chloroisopropyl) ether .................................................................................... | 34283 | 108–60–1 | 042 B | 012 B |
| Bis(2-ethylhexyl) phthalate ..................................................................................... | 39100 | 117–81–7 | 066 B | 013 B |
| 4-bromophenyl phenyl ether ................................................................................... | 34636 | 101–55–3 | 041 B | 014 B |
| Butyl benzyl phthalate ............................................................................................ | 34292 | 85–68–7 | 067 B | 015 B |
| n-C10 (Appendix C) ................................................................................................ | 77427 | 124–18–5 | 517 B |  |
| n-C12 (Appendix C) ................................................................................................ | 77588 | 112–40–2 | 506 B |  |
| n-C14 (Appendix C) ................................................................................................ | 77691 | 629–59–4 | 518 B |  |
| n-C16 (Appendix C) ................................................................................................ | 77757 | 544–76–3 | 519 B |  |
| n-C18 (Appendix C) ................................................................................................ | 77804 | 593–45–3 | 520 B |  |
| n-C20 (Appendix C) ................................................................................................ | 77830 | 112–95–8 | 521 B |  |
| n-C22 (Appendix C) ................................................................................................ | 77859 | 629–97–0 | 522 B |  |
| n-C24 (Appendix C) ................................................................................................ | 77886 | 646–31–1 | 523 B |  |
| n-C26 (Appendix C) ................................................................................................ | 77901 | 630–01–3 | 524 B |  |
| n-C28 (Appendix C) ................................................................................................ | 78116 | 630–02–4 | 525 B |  |
| n-C30 (Appendix C) ................................................................................................ | 78117 | 638–68–6 | 526 B |  |
| Carbazole (4c) ........................................................................................................ | 77571 | 86–74–8 | 528 B |  |
| 2-chloronaphthalene ............................................................................................... | 34581 | 91–58–7 | 020 B | 016 B |
| 4-chlorophenyl phenyl ether ................................................................................... | 34641 | 7005–72–3 | 040 B | 017 B |
| Chrysene ................................................................................................................ | 34320 | 218–01–9 | 076 B | 018 B |
| P-cymene (Appendix C) ......................................................................................... | 77356 | 99–87–6 | 513 B |  |
| Dibenzo(a,h)anthracene ......................................................................................... | 34556 | 53–70–3 | 082 B | 019 B |
| Dibenzofuran (Appendix C and 4c) ........................................................................ | 81302 | 132–64–9 | 505 B |  |
| Dibenzothiophene (Synfuel) ................................................................................... | 77639 | 132–65–0 | 504 B |  |
| Di-n-butyl phthalate ................................................................................................ | 39110 | 84–74–2 | 068 B | 026 B |
| 1,2-dichlorobenzene ............................................................................................... | 34536 | 95–50–1 | 025 B | 020 B |
| 1,3-dichlorobenzene ............................................................................................... | 34566 | 541–73–1 | 026 B | 021 B |
| 1,4-dichlorobenzene ............................................................................................... | 34571 | 106–46–7 | 027 B | 022 B |
| 3,3-dichlorobenzidine ............................................................................................. | 34631 | 91–94–1 | 028 B | 023 B |
| Diethyl phthalate ..................................................................................................... | 34336 | 84–66–2 | 070 B | 024 B |
| 2,4-dimethylphenol ................................................................................................. | 34606 | 105–67–9 | 034 A | 003 A |
| Dimethyl phthalate .................................................................................................. | 34341 | 131–11–3 | 071 B | 025 B |
| 2,4-dinitrotoluene .................................................................................................... | 34611 | 121–14–2 | 035 B | 027 B |
| 2,6-dinitrotoluene .................................................................................................... | 34626 | 606–20–2 | 036 B | 028 B |
| Di-n-octyl phthalate ................................................................................................. | 34596 | 117–84–0 | 069 B | 029 B |
| Diphenylamine (Appendix C) .................................................................................. | 77579 | 122–39–4 | 507 B |  |
| Diphenyl ether (Appendix C) .................................................................................. | 77587 | 101–84–8 | 508 B |  |
| 1,2-diphenylhydrazine ............................................................................................. | 34346 | 122–66–7 | 037 B | 030 B |
| Fluoranthene ........................................................................................................... | 34376 | 206–44–0 | 039 B | 031 B |
| Fluorene .................................................................................................................. | 34381 | 86–73–7 | 080 B | 032 B |
| Hexachlorobenzene ................................................................................................ | 39700 | 118–74–1 | 009 B | 033 B |
| Hexachlorobutadiene .............................................................................................. | 34391 | 87–68–3 | 052 B | 034 B |
| Hexachloroethane ................................................................................................... | 34396 | 67–72–1 | 012 B | 036 B |
| Hexachlorocyclopentadiene .................................................................................... | 34386 | 77–47–4 | 053 B | 035 B |
| Indeno(1,2,3-cd)pyrene .......................................................................................... | 34403 | 193–39–5 | 083 B | 037 B |
| Isophorone .............................................................................................................. | 34408 | 78–59–1 | 054 B | 038 B |
| Naphthalene ........................................................................................................... | 34696 | 91–20–3 | 055 B | 039 B |
| B-naphthylamine (Appendix C) .............................................................................. | 82553 | 91–59–8 | 502 B |  |
| Nitrobenzene .......................................................................................................... | 34447 | 98–95–3 | 056 B | 040 B |
| N-nitrosodimethylamine .......................................................................................... | 34438 | 62–75–9 | 061 B | 041 B |
| N-nitrosodi-n-propylamine ...................................................................................... | 34428 | 621–64–7 | 063 B | 042 B |
| N-nitrosodiphenylamine .......................................................................................... | 34433 | 86–30–3 | 062 B | 043 B |

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1625

TABLE 1—BASE/NEUTRAL EXTRACTABLE COMPOUNDS—Continued

| Compound | STORET | CAS reg- istry | EPA- EGD | NPDES |
| --- | --- | --- | --- | --- |
| Phenanthrene ......................................................................................................... | 34461 | 85–01–8 | 081 B | 044 B |
| Phenol ..................................................................................................................... | 34694 | 108–95–2 | 065 A | 010 A |
| a-Picoline (Synfuel) ................................................................................................ | 77088 | 109–06–89 | 503 B |  |
| Pyrene .................................................................................................................... | 34469 | 129–00–0 | 084 B | 045 B |
| styrene (Appendix C) .............................................................................................. | 77128 | 100–42–5 | 510 B |  |
| a-terpineol (Appendix C) ........................................................................................ | 77493 | 98–55–5 | 509 B |  |
| 1,2,3-trichlorobenzene (4c) ..................................................................................... | 77613 | 87–61–6 | 529 B |  |
| 1,2,4-trichlorobenzene ............................................................................................ | 34551 | 120–82–1 | 008 B | 046 B |

TABLE 2—ACID EXTRACTABLE COMPOUNDS

| Compound | STORET | CAS reg- istry | EPA- EGD | NPDES |
| --- | --- | --- | --- | --- |
| 4-chloro-3-methylphenol ......................................................................................... | 34452 | 59–50–7 | 022 A | 008 A |
| 2-chlorophenol ........................................................................................................ | 34586 | 95–57–8 | 024 A | 001 A |
| 2,4-dichlorophenol .................................................................................................. | 34601 | 120–83–2 | 031 A | 002 A |
| 2,4-dinitrophenol ..................................................................................................... | 34616 | 51–28–5 | 059 A | 005 A |
| 2-methyl-4,6-dinitrophenol ...................................................................................... | 34657 | 534–52–1 | 060 A | 004 A |
| 2-nitrophenol ........................................................................................................... | 34591 | 88–75–5 | 057 A | 006 A |
| 4-nitrophenol ........................................................................................................... | 34646 | 100–02–7 | 058 A | 007 A |
| Pentachlorophenol .................................................................................................. | 39032 | 87–86–5 | 064 A | 009 A |
| 2,3,6-trichlorophenol (4c) ........................................................................................ | 77688 | 93–37–55 | 530 A |  |
| 2,4,5-trichlorophenol (4c) ........................................................................................ | .............. | 95–95–4 | 531 A |  |
| 2,4,6-trichlorophenol ............................................................................................... | 34621 | 88–06–2 | 021 A | 011 A |

TABLE 3—GAS CHROMATOGRAPHY OF BASE/NEUTRAL EXTRACTABLE COMPOUNDS

| EGD No. 1 | Compound | Retention time | Detec- tion limit 2 (g/L) |
| --- | --- | --- | --- |
|  |  | Mean (sec) | EGD Ref | Relative |  |
| 164 | 2,2-difluorobiphenyl (int std) ................................................................ | 1163 | 164 | 1.000–1.000 | 10 |
| 061 | N-nitrosodimethylamine ........................................................................ | 385 | 164 | ns | 50 |
| 603 | alpha picoline-d7 ................................................................................... | 417 | 164 | 0.326–0.393 | 50 |
| 703 | alpha picoline ........................................................................................ | 426 | 603 | 1.006–1.028 | 50 |
| 610 | styrene-d5 ............................................................................................. | 546 | 164 | 0.450–0.488 | 10 |
| 710 | styrene .................................................................................................. | 549 | 610 | 1.002–1.009 | 10 |
| 613 | p-cymene-d14 ....................................................................................... | 742 | 164 | 0.624–0.652 | 10 |
| 713 | p-cymene .............................................................................................. | 755 | 613 | 1.008–1.023 | 10 |
| 265 | phenol-d5 .............................................................................................. | 696 | 164 | 0.584–0.613 | 10 |
| 365 | phenol ................................................................................................... | 700 | 265 | 0.995–1.010 | 10 |
| 218 | bis(2-chloroethyl) ether-d8 .................................................................... | 696 | 164 | 0.584–0.607 | 10 |
| 318 | bis(2-chloroethyl) ether ......................................................................... | 704 | 218 | 1.007–1.016 | 10 |
| 617 | n-decane-d22 ........................................................................................ | 698 | 164 | 0.585–0.615 | 10 |
| 717 | n-decane ............................................................................................... | 720 | 617 | 1.022–1.038 | 10 |
| 226 | 1,3-dichlorobenzene-d4 ........................................................................ | 722 | 164 | 0.605–0.636 | 10 |
| 326 | 1,3-dichlorobenzene .............................................................................. | 724 | 226 | 0.998–1.008 | 10 |
| 227 | 1,4-dichlorobenzene-d4 ........................................................................ | 737 | 164 | 0.601–0.666 | 10 |
| 327 | 1,4-dichlorobenzene .............................................................................. | 740 | 227 | 0.997–1.009 | 10 |
| 225 | 1,2-dichlorobenzene-d4 ........................................................................ | 758 | 164 | 0.632–0.667 | 10 |
| 325 | 1,2-dichlorobenzene .............................................................................. | 760 | 225 | 0.995–1.008 | 10 |
| 242 | bis(2-chloroisopropyl) ether-d12 ........................................................... | 788 | 164 | 0.664–0.691 | 10 |
| 342 | bis(2-chloroisopropyl) ether .................................................................. | 799 | 242 | 1.010–1.016 | 10 |
| 212 | hexachloroethane-13C .......................................................................... | 819 | 164 | 0.690–0.717 | 10 |
| 312 | hexachloroethane ................................................................................. | 823 | 212 | 0.999–1.001 | 10 |
| 063 | N-nitrosodi-n-propylamine ..................................................................... | 830 | 164 | ns | 20 |
| 256 | nitrobenzene-d5 .................................................................................... | 845 | 164 | 0.706–0.727 | 10 |
| 356 | nitrobenzene ......................................................................................... | 849 | 256 | 1.002–1.007 | 10 |
| 254 | isophorone-d8 ....................................................................................... | 881 | 164 | 0.747–0.767 | 10 |
| 354 | isophorone ............................................................................................ | 889 | 254 | 0.999–1.017 | 10 |
| 234 | 2,4-dimethyl phenol-d3 ......................................................................... | 921 | 164 | 0.781–0.803 | 10 |
| 334 | 2,4-dimethylphenol ................................................................................ | 924 | 234 | 0.999–1.003 | 10 |
| 043 | bis(2-chloroethoxy) methane ................................................................ | 939 | 164 | ns | 10 |
| 208 | 1,2,4-trichlorobenzene-d3 ..................................................................... | 955 | 164 | 0.813–0.830 | 10 |
| 308 | 1,2,4-trichlorobenzene .......................................................................... | 958 | 208 | 1.000–1.005 | 10 |
| 255 | naphthalene-d8 ..................................................................................... | 963 | 164 | 0.819–0.836 | 10 |
| 355 | naphthalene .......................................................................................... | 967 | 255 | 1.001–1.006 | 10 |
| 609 | alpha-terpineol-d3 ................................................................................. | 973 | 164 | 0.829–0.844 | 10 |

#### Pt. 136, App. A, Meth. 1625

40 CFR Ch. I (7–1–17 Edition)

TABLE 3—GAS CHROMATOGRAPHY OF BASE/NEUTRAL EXTRACTABLE COMPOUNDS—Continued

| EGD No. 1 | Compound | Retention time | Detec- tion limit 2 (g/L) |
| --- | --- | --- | --- |
|  |  | Mean (sec) | EGD Ref | Relative |  |
| 709 | alpha-terpineol ...................................................................................... | 975 | 609 | 0.998–1.008 | 10 |
| 606 | n-dodecane-d26 .................................................................................... | 953 | 164 | 0.730–0.908 | 10 |
| 706 | n-dodecane ........................................................................................... | 981 | 606 | 0.986–1.051 | 10 |
| 529 | 1,2,3-trichlorobenzene .......................................................................... | 1003 | 164 | ns | 10 |
| 252 | hexachlorobutadiene-13C4 ................................................................... | 1005 | 164 | 0.856–0.871 | 10 |
| 352 | hexachlorobutadiene ............................................................................. | 1006 | 252 | 0.999–1.002 | 10 |
| 253 | hexachlorocyclopentadiene-13C4 ......................................................... | 1147 | 164 | 0.976–0.986 | 10 |
| 353 | hexachlorocyclopentadiene ................................................................... | 1142 | 253 | 0.999–1.001 | 10 |
| 220 | 2-chloronaphthalene-d7 ........................................................................ | 1185 | 164 | 1.014–1.024 | 10 |
| 320 | 2-chloronaphthalene ............................................................................. | 1200 | 220 | 0.997–1.007 | 10 |
| 518 | n-tetradecane ........................................................................................ | 1203 | 164 | ns | 10 |
| 612 | Biphenyl-d10 ......................................................................................... | 1205 | 164 | 1.016–1.027 | 10 |
| 712 | Biphenyl ................................................................................................ | 1195 | 612 | 1.001–1.006 | 10 |
| 608 | Diphenyl ether-d10 ................................................................................ | 1211 | 164 | 1.036–1.047 | 10 |
| 708 | Diphenyl ether ....................................................................................... | 1216 | 608 | 0.997–1.009 | 10 |
| 277 | Acenaphthylene-d8 ............................................................................... | 1265 | 164 | 1.080–1.095 | 10 |
| 377 | Acenaphthylene .................................................................................... | 1247 | 277 | 1.000–1.004 | 10 |
| 271 | Dimethyl phthalate-d4 ........................................................................... | 1269 | 164 | 1.083–1.102 | 10 |
| 371 | Dimethyl phthalate ................................................................................ | 1273 | 271 | 0.998–1.005 | 10 |
| 236 | 2,6-dinitrotoluene-d3 ............................................................................. | 1283 | 164 | 1.090–1.112 | 10 |
| 336 | 2,6-dinitrotoluene .................................................................................. | 1300 | 236 | 1.001–1.005 | 10 |
| 201 | Acenaphthene-d10 ................................................................................ | 1298 | 164 | 1.107–1.125 | 10 |
| 301 | Acenaphthene ....................................................................................... | 1304 | 201 | 0.999–1.009 | 10 |
| 605 | Dibenzofuran-d8 ................................................................................... | 1331 | 164 | 1.134–1.155 | 10 |
| 705 | Dibenzofuran ......................................................................................... | 1335 | 605 | 0.998–1.007 | 10 |
| 602 | Beta-naphthylamine-d7 ......................................................................... | 1368 | 164 | 1.163–1.189 | 50 |
| 702 | Beta-naphthylamine .............................................................................. | 1371 | 602 | 0.996–1.007 | 50 |
| 280 | Fluorene-d10 ......................................................................................... | 1395 | 164 | 1.185–1.214 | 10 |
| 380 | Fluorene ................................................................................................ | 1401 | 281 | 0.999–1.008 | 10 |
| 240 | 4-chlorophenyl phenyl ether-d5 ............................................................ | 1406 | 164 | 1.194–1.223 | 10 |
| 340 | 4-chlorophenyl phenyl ether ................................................................. | 1409 | 240 | 0.990–1.015 | 10 |
| 270 | Diethyl phthalate-d4 .............................................................................. | 1409 | 164 | 1.197–1.229 | 10 |
| 370 | Diethyl phthalate ................................................................................... | 1414 | 270 | 0.996–1.006 | 10 |
| 619 | n-hexadecane-d34 ................................................................................ | 1447 | 164 | 1.010–1.478 | 10 |
| 719 | n-hexadecane ....................................................................................... | 1469 | 619 | 1.013–1.020 | 10 |
| 235 | 2,4-dinitrotoluene-d3 ............................................................................. | 1359 | 164 | 1.152–1.181 | 10 |
| 335 | 2,4-dinitrotoluene .................................................................................. | 1344 | 235 | 1.000–1.002 | 10 |
| 237 | 1,2-diphenylhydrazine-d8 ...................................................................... | 1433 | 164 | 1.216–1.248 | 20 |
| 337 | 1,2-diphenylhydrazine (3) ...................................................................... | 1439 | 237 | 0.999–1.009 | 20 |
| 607 | Diphenylamine-d10 ............................................................................... | 1437 | 164 | 1.213–1.249 | 20 |
| 707 | Diphenylamine ...................................................................................... | 1439 | 607 | 1.000–1.007 | 20 |
| 262 | N-nitrosodiphenylamine-d6 ................................................................... | 1447 | 164 | 1.225–1.252 | 20 |
| 362 | N-nitrosodiphenylamine (4) ................................................................... | 1464 | 262 | 1.000–1.002 | 20 |
| 041 | 4-bromophenyl phenyl ether ................................................................. | 1498 | 164 | 1.271–1.307 | 10 |
| 209 | Hexachlorobenzene-13C6 .................................................................... | 1521 | 164 | 1.288–1.327 | 10 |
| 309 | Hexachlorobenzene .............................................................................. | 1522 | 209 | 0.999–1.001 | 10 |
| 281 | Phenanthrene-d10 ................................................................................ | 1578 | 164 | 1.334–1.380 | 10 |
| 520 | n-octadecane ........................................................................................ | 1580 | 164 | ns | 10 |
| 381 | Phenanthrene ....................................................................................... | 1583 | 281 | 1.000–1.005 | 10 |
| 278 | Anthracene-d10 ..................................................................................... | 1588 | 164 | 1.342–1.388 | 10 |
| 378 | Anthracene ............................................................................................ | 1592 | 278 | 0.998–1.006 | 10 |
| 604 | Dibenzothiophene-d8 ............................................................................ | 1559 | 164 | 1.314–1.361 | 10 |
| 704 | Dibenzothiophene ................................................................................. | 1564 | 604 | 1.000–1.006 | 10 |
| 528 | Carbazole .............................................................................................. | 1650 | 164 | ns | 20 |
| 621 | n-eicosane-d42 ..................................................................................... | 1655 | 164 | 1.184–1.662 | 10 |
| 721 | n-eicosane ............................................................................................. | 1677 | 621 | 1.010–1.021 | 10 |
| 268 | Di-n-butyl phthalate-d4 .......................................................................... | 1719 | 164 | 1.446–1.510 | 10 |
| 368 | Di-n-butyl phthalate ............................................................................... | 1723 | 268 | 1.000–1.003 | 10 |
| 239 | Fluoranthene-d10 .................................................................................. | 1813 | 164 | 1.522–1.596 | 10 |
| 339 | Fluoranthene ......................................................................................... | 1817 | 239 | 1.000–1.004 | 10 |
| 284 | Pyrene-d10 ........................................................................................... | 1844 | 164 | 1.523–1.644 | 10 |
| 384 | Pyrene ................................................................................................... | 1852 | 284 | 1.001–1.003 | 10 |
| 205 | Benzidine-d8 ......................................................................................... | 1854 | 164 | 1.549–1.632 | 50 |
| 305 | Benzidine .............................................................................................. | 1853 | 205 | 1.000–1.002 | 50 |
| 522 | n-docosane ........................................................................................... | 1889 | 164 | ns | 10 |
| 623 | n-tetracosane-d50 ................................................................................. | 1997 | 164 | 1.671–1.764 | 10 |
| 723 | n-tetracosane ........................................................................................ | 2025 | 612 | 1.012–1.015 | 10 |
| 067 | Butylbenzyl phthalate ............................................................................ | 2060 | 164 | ns | 10 |
| 276 | Chrysene-d12 ........................................................................................ | 2081 | 164 | 1.743–1.837 | 10 |
| 376 | Chrysene ............................................................................................... | 2083 | 276 | 1.000–1.004 | 10 |

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1625

TABLE 3—GAS CHROMATOGRAPHY OF BASE/NEUTRAL EXTRACTABLE COMPOUNDS—Continued

| EGD No. 1 | Compound | Retention time | Detec- tion limit 2 (g/L) |
| --- | --- | --- | --- |
|  |  | Mean (sec) | EGD Ref | Relative |  |
| 272 | Benzo(a)anthracene-d12 ...................................................................... | 2082 | 164 | 1.735–1.846 | 10 |
| 372 | Benzo(a)anthracene .............................................................................. | 2090 | 272 | 0.999–1.007 | 10 |
| 228 | 3,3-dichlorobenzidine-d6 ...................................................................... | 2088 | 164 | 1.744–1.848 | 50 |
| 328 | 3,3-dichlorobenzidine ........................................................................... | 2086 | 228 | 1.000–1.001 | 50 |
| 266 | Bis(2-ethylhexyl) phthalate-d4 .............................................................. | 2123 | 164 | 1.771–1.880 | 10 |
| 366 | Bis(2-ethylhexyl) phthalate .................................................................... | 2124 | 266 | 1.000–1.002 | 10 |
| 524 | n-hexacosane ........................................................................................ | 2147 | 164 | ns | 10 |
| 269 | di-n-octyl phthalate-d4 .......................................................................... | 2239 | 164 | 1.867–1.982 | 10 |
| 369 | di-n-octyl phthalate ................................................................................ | 2240 | 269 | 1.000–1.002 | 10 |
| 525 | n-octacosane ........................................................................................ | 2272 | 164 | ns | 10 |
| 274 | Benzo(b)fluoranthene-d12 .................................................................... | 2281 | 164 | 1.902–2.025 | 10 |
| 354 | Benzo(b)fluoranthene ............................................................................ | 2293 | 274 | 1.000–1.005 | 10 |
| 275 | Benzo(k)fluoranthene-d12 ..................................................................... | 2287 | 164 | 1.906–2.033 | 10 |
| 375 | Benzo(k)fluoranthene ............................................................................ | 2293 | 275 | 1.000–1.005 | 10 |
| 273 | Benzo(a)pyrene-d12 ............................................................................. | 2351 | 164 | 1.954–2.088 | 10 |
| 373 | Benzo(a)pyrene ..................................................................................... | 2350 | 273 | 1.000–1.004 | 10 |
| 626 | N-triacontane-d62 ................................................................................. | 2384 | 164 | 1.972–2.127 | 10 |
| 726 | N-triacontane ........................................................................................ | 2429 | 626 | 1.011–1.028 | 10 |
| 083 | Indeno(1,2,3-cd)pyrene ......................................................................... | 2650 | 164 | ns | 20 |
| 082 | Dibenzo(a,h)anthracene ........................................................................ | 2660 | 164 | ns | 20 |
| 279 | Benzo(ghi)perylene-d12 ........................................................................ | 2741 | 164 | 2.187–2.524 | 20 |
| 379 | Benzo(ghi)perylene ............................................................................... | 2750 | 279 | 1.001–1.006 | 20 |

1 Reference numbers beginning with 0, 1 or 5 indicate a pollutant quantified by the internal standard method; reference num- bers beginning with 2 or 6 indicate a labeled compound quantified by the internal standard method; reference numbers beginning with 3 or 7 indicate a pollutant quantified by isotope dilution.

2 This is a minimum level at which the entire GC/MS system must give recognizable mass spectra (background corrected) and acceptable calibration points.

3 Detected as azobenzene.

4 Detected as diphenylamine.

ns = specification not available at time of release of method.

Column: 30 2 m 0.25 0.02 mm i.d. 94% methyl, 4% phenyl, 1% vinyl bonded phase fused silica capillary. Temperature program: 5 min at 30 C; 30 – 280 C at 8 C per min; isothermal at 280 C until benzo(ghi)perylene elutes. Gas velocity: 30 5 cm/sec.

TABLE 4—GAS CHROMATOGRAPHY OF ACID EXTRACTABLE COMPOUNDS

| EGD No. 1 | Compound | Retention time | Detec- tion limit 2 (g/L) |
| --- | --- | --- | --- |
|  |  | Mean (sec) | EGD Ref | Relative |  |
| 164 | 2,2-difluorobiphenyl (int std) ................................................................ | 1163 | 164 | 1.000–1.000 | 10 |
| 224 | 2-chlorophenol-d4 ................................................................................. | 701 | 164 | 0.587–0.618 | 10 |
| 324 | 2-chlorophenol ...................................................................................... | 705 | 224 | 0.997–1.010 | 10 |
| 257 | 2-nitrophenol-d4 .................................................................................... | 898 | 164 | 0.761–0.783 | 20 |
| 357 | 2-nitrophenol ......................................................................................... | 900 | 257 | 0.994–1.009 | 20 |
| 231 | 2,4-dichlorophenol-d3 ........................................................................... | 944 | 164 | 0.802–0.822 | 10 |
| 331 | 2,4-dichlorophenol ................................................................................. | 947 | 231 | 0.997–1.006 | 10 |
| 222 | 4-chloro-3-methylphenol-d2 .................................................................. | 1086 | 164 | 0.930–0.943 | 10 |
| 322 | 4-chloro-3-methylphenol ....................................................................... | 1091 | 222 | 0.998–1.003 | 10 |
| 221 | 2,4,6-trichlorophenol-d2 ........................................................................ | 1162 | 164 | 0.994–1.005 | 10 |
| 321 | 2,4,6-trichlorophenol ............................................................................. | 1165 | 221 | 0.998–1.004 | 10 |
| 531 | 2,4,5-trichlorophenol ............................................................................. | 1170 | 164 | ns | 10 |
| 530 | 2,3,6-trichlorophenol ............................................................................. | 1195 | 164 | ns | 10 |
| 259 | 2,4-dinitrophenol-d3 .............................................................................. | 1323 | 164 | 1.127–1.149 | 50 |
| 359 | 2,4-dinitrophenol ................................................................................... | 1325 | 259 | 1.000–1.005 | 50 |
| 258 | 4-nitrophenol-d4 .................................................................................... | 1349 | 164 | 1.147–1.175 | 50 |
| 358 | 4-nitrophenol ......................................................................................... | 1354 | 258 | 0.997–1.006 | 50 |
| 260 | 2-methyl-4,6-dinitrophenol-d2 ............................................................... | 1433 | 164 | 1.216–1.249 | 20 |
| 360 | 2-methyl-4,6-dinitrophenol .................................................................... | 1435 | 260 | 1.000–1.002 | 20 |
| 264 | Pentachlorophenol-13C6 ...................................................................... | 1559 | 164 | 1.320–1.363 | 50 |
| 364 | Pentachlorophenol ................................................................................ | 1561 | 264 | 0.998–1.002 | 50 |

1 Reference numbers beginning with 0, 1 or 5 indicate a pollutant quantified by the internal standard method; reference num- bers beginning with 2 or 6 indicate a labeled compound quantified by the internal standard method; reference numbers beginning with 3 or 7 indicate a pollutant quantified by isotope dilution.

2 This is a minimum level at which the entire GC/MS system must give recognizable mass spectra (background corrected) and acceptable calibration points.

ns = specification not available at time of release of method.

Column: 30 2m 0.25 0.02mm i.d. 94% methyl, 4% phenyl, 1% vinyl bonded phase fused silica capillary. Temperature program: 5 min at 30 C; 8 C/min. to 250 C or until pentachlorophenol elutes.

Gas velocity: 30 5 cm/sec.

#### Pt. 136, App. A, Meth. 1625

TABLE 5—DFTPP MASS INTENSITY SPECIFICATIONS

#### 40 CFR Ch. I (7–1–17 Edition)

TABLE 6—BASE/NEUTRAL EXTRACTABLE COM-

POUND CHARACTERISTIC MASSES—Continued

| Mass | Intensity required |
| --- | --- |
| 51 | 30–60 percent of mass 198. |
| 68 | Less than 2 percent of mass 69. |
| 70 | Less than 2 percent of mass 69. |
| 127 | 40–60 percent of mass 198. |
| 197 | Less than 1 percent of mass 198. |
| 199 | 5–9 percent of mass 198. |
| 275 | 10–30 percent of mass 198. |
| 365 | greater than 1 percent of mass 198 |
| 441 | present and less than mass 443 |
| 442 | 40–100 percent of mass 198. |
| 443 | 17–23 percent of mass 442. |

| Compound | Labeled analog | Primary m/ z |
| --- | --- | --- |
| 1,4-dichlorobenzene ........................ | d4 | 146/152 |
| 3,3-dichlorobenzidine ...................... | d6 | 252/258 |
| Diethyl phthalate .............................. | d4 | 149/153 |
| 2,4-dimethylphenol .......................... | d3 | 122/125 |
| Dimethyl phthalate ........................... | d4 | 163/167 |
| 2,4-dinitrotoluene ............................. | d3 | 164/168 |
| 2,6-dinitrotoluene ............................. | d3 | 165/167 |
| Di-n-octyl phthalate ......................... | d4 | 149/153 |
| Diphenylamine ................................. | d10 | 169/179 |
| Diphenyl ether ................................. | d10 | 170/180 |
| 1,2-diphenylhydrazine 1 ................... | d10 | 77/82 |
| Fluoranthene ................................... | d10 | 202/212 |
| Fluorene .......................................... | d10 | 166/176 |
| Hexachlorobenzene ......................... | 13C6 | 284/292 |
| Hexachlorobutadiene ....................... | 13C4 | 225/231 |
| Hexachloroethane ........................... | 13C | 201/204 |
| Hexachlorocyclopentadiene ............. | 13C4 | 237/241 |
| Ideno(1,2,3-cd)pyrene ..................... | ................ | 276 |
| Isophorone ....................................... | d8 | 82/88 |
| Naphthalene .................................... | d8 | 128/136 |
| B-naphthylamine .............................. | d7 | 143/150 |
| Nitrobenzene ................................... | d5 | 123/128 |
| N-nitrosodimethylamine ................... | ................ | 74 |
| N-nitrosodi-n-propylamine ............... | ................ | 70 |
| N-nitrosodiphenylamile 2 .................. | d6 | 169/175 |
| Phenanthrene .................................. | d10 | 178/188 |
| Phenol ............................................. | d5 | 94/71 |
| a-picoline ......................................... | d7 | 93/100 |
| Pyrene ............................................. | d10 | 202/212 |
| Styrene ............................................ | d5 | 104/109 |
| a-terpineol ........................................ | d3 | 59/62 |
| 1,2,3-trichlorobenzene ..................... | d3 | 180/183 |
| 1,2,4-trichlorobenzene ..................... | d3 | 180/183 |

TABLE 6—BASE/NEUTRAL EXTRACTABLE COMPOUND CHARACTERISTIC MASSES

| Compound | Labeled analog | Primary m/ z |
| --- | --- | --- |
| Acenaphthene ................................. | d10 | 154/164 |
| Acenaphthylene ............................... | d8 | 152/160 |
| Anthracene ...................................... | d10 | 178/188 |
| Benzidine ......................................... | d8 | 184/192 |
| Benzo(a)anthracene ........................ | d12 | 228/240 |
| Benzo(b)fluoranthene ...................... | d12 | 252/264 |
| Benzo(k)fluoranthene ...................... | d12 | 252/264 |
| Benzo(a)pyrene ............................... | d12 | 252/264 |
| Benzo(ghi)perylene ......................... | d12 | 276/288 |
| Biphenyl ........................................... | d10 | 154/164 |
| Bis(2-chloroethyl) ether ................... | d8 | 93/101 |
| Bis(2-chloroethoxy)methane ............ | ................ | 93 |
| Bis(2-chloroisopropyl) ether ............. | d12 | 121/131 |
| Bis(2-ethylhexyl) phthalate .............. | d4 | 149/153 |
| 4-bromophenyl phenyl ether ........... | ................ | 248 |
| Butyl benzyl phthalate ..................... | ................ | 149 |
| n-C10 ............................................... | d22 | 55/66 |
| n-C12 ............................................... | d26 | 55/66 |
| n-C14 ............................................... | ................ | 55 |
| n-C16 ............................................... | d34 | 55/66 |
| n-C18 ............................................... | ................ | 55 |
| n-C20 ............................................... | d42 | 55/66 |
| n-C22 ............................................... | ................ | 55 |
| n-C24 ............................................... | d50 | 55/66 |
| n-C26 ............................................... | ................ | 55 |
| n-C28 ............................................... | ................ | 55 |
| n-C30 ............................................... | d62 | 55/66 |
| Carbazole ........................................ | d8 | 167/175 |
| 2-chloronaphthalene ........................ | d7 | 162/169 |
| 4-chlorophenyl phenyl ether ............ | d5 | 204/209 |
| Chrysene ......................................... | d12 | 228/240 |
| p-cymene ......................................... | d14 | 114/130 |
| Dibenzo(a,h)anthracene .................. | ................ | 278 |
| Dibenzofuran ................................... | d8 | 168/176 |
| Dibenzothiophene ............................ | d8 | 184/192 |
| Di-n-butyl phthalate ......................... | d4 | 149/153 |
| 1,2-dichlorobenzene ........................ | d4 | 146/152 |
| 1,3-dichlorobenzene ........................ | d4 | 146/152 |

1 Detected as azobenzene.

2 Detected as diphenylamine.

TABLE 7—ACID EXTRACTABLE COMPOUND CHARACTERISTIC MASSES

| Compound | Labeled analog | Primary m/ z |
| --- | --- | --- |
| 4-chloro-3-methylphenol .................. | d2 | 107/109 |
| 2-chlorophenol ................................. | d4 | 128/132 |
| 2,4-dichlorophenol ........................... | d3 | 162/167 |
| 2,4-dinitrophenol .............................. | d3 | 184/187 |
| 2-methyl-4,6-dinitrophenol ............... | d2 | 198/200 |
| 2-nitrophenol .................................... | d4 | 139/143 |
| 4-nitrophenol .................................... | d4 | 139/143 |
| Pentachlorophenol ........................... | 13C6 | 266/272 |
| 2,3,6-trichlorophenol ........................ | d2 | 196/200 |
| 2,4,5-trichlorophenol ........................ | d2 | 196/200 |
| 2,4,6-trichlorophenol ........................ | d2 | 196/200 |

TABLE 8—ACCEPTANCE CRITERIA FOR PERFORMANCE TESTS

| EGD No. 1 | Compound | Acceptance criteria |
| --- | --- | --- |
|  |  | Initial precision and ac- curacy section 8.2.3 (g/L) | Labeled com- pound recov- ery sec. 8.3 and 14.2 P (percent) | Calibration verification sec. 12.5 (g/mL) | On-going accuracy sec. 11.6 R (g/L) |
|  |  | s | X |  |  |  |
| 301 201 377 277 | Acenaphthene ................................................... Acenaphthene-d10 ............................................ Acenaphtylene .................................................. Acenaphthylene-d8 ........................................... | 21 38 38 31 | 79–134 38–147 69–186 38–146 | ........................ 20–270 ........................ 23–239 | 80–125 71–141 60–166 66–152 | 72–144 30–180 61–207 33–168 |

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1625

TABLE 8—ACCEPTANCE CRITERIA FOR PERFORMANCE TESTS—Continued

| EGD No. 1 | Compound | Acceptance criteria |
| --- | --- | --- |
|  |  | Initial precision and ac- curacy section 8.2.3 (g/L) | Labeled com- pound recov- ery sec. 8.3 and 14.2 P (percent) | Calibration verification sec. 12.5 (g/mL) | On-going accuracy sec. 11.6 R (g/L) |
|  |  | s | X |  |  |  |
| 378 | Anthracene ........................................................ | 41 | 58–174 | ........................ | 60–168 | 50–199 |
| 278 | Anthracene-d10 ................................................. | 49 | 31–194 | 14–419 | 58–171 | 23–242 |
| 305 | Benzidine .......................................................... | 119 | 16–518 | ........................ | 34–296 | 11–672 |
| 205 | Benzidine-d8 ..................................................... | 269 | ns-ns | ns-ns | ns-ns | ns-ns |
| 372 | Benzo(a)anthracene .......................................... | 20 | 65–168 | ........................ | 70–142 | 62–176 |
| 272 | Benzo(a)anthracene-d12 .................................. | 41 | 25–298 | 12–605 | 28–357 | 22–329 |
| 374 | Benzo(b)fluoranthene ........................................ | 183 | 32–545 | ........................ | 61–164 | 20–ns |
| 274 | Benzo(b)fluoranthene-d12 ................................ | 168 | 11–577 | ns-ns | 14–ns | ns-ns |
| 375 | Benzo(k)fluoranthene ........................................ | 26 | 59–143 | ........................ | 13–ns | 53–155 |
| 275 | Benzo(k)fluoranthene-d12 ................................. | 114 | 15–514 | ns-ns | 13–ns | ns–685 |
| 373 | Benzo(a)pyrene ................................................. | 26 | 62–195 | ........................ | 78–129 | 59–206 |
| 273 | Benzo(a)pyrene-d12 ......................................... | 24 | 35–181 | 21–290 | 12–ns | 32–194 |
| 379 | Benzo(ghi)perylene ........................................... | 21 | 72–160 | ........................ | 69–145 | 58–168 |
| 279 | Benzo(ghi)perylene-d12 .................................... | 45 | 29–268 | 14–529 | 13–ns | 25–303 |
| 712 | Biphenyl (Appendix C) ...................................... | 41 | 75–148 | ........................ | 58–171 | 62–176 |
| 612 | Biphenyl-d12 ..................................................... | 43 | 28–165 | ns-ns | 52–192 | 17–267 |
| 318 | Bis(2-chloroethyl) ether ..................................... | 34 | 55–196 | ........................ | 61–164 | 50–213 |
| 218 | Bis(2-chloroethyl) ether-d8 ................................ | 33 | 29–196 | 15–372 | 52–194 | 25–222 |
| 043 | Bis(2-chloroethoxy)methane* ............................ | 27 | 43–153 | ........................ | 44–228 | 39–166 |
| 342 | Bis(2-chloroisopropyl) ether .............................. | 17 | 81–138 | ........................ | 67–148 | 77–145 |
| 242 | Bis(2-chloroisopropyl)ether-d12 ........................ | 27 | 35–149 | 20–260 | 44–229 | 30–169 |
| 366 | Bis(2-ethylhexyl) phthalate ................................ | 31 | 69–220 | ........................ | 76–131 | 64–232 |
| 266 | Bis(2-ethylhexyl) phthalate-d4 .......................... | 29 | 32–205 | 18–364 | 43–232 | 28–224 |
| 041 | 4-bromophenyl phenyl ether* ............................ | 44 | 44–140 | ........................ | 52–193 | 35–172 |
| 067 | Butyl benzyl phthalate* ..................................... | 31 | 19–233 | ........................ | 22–450 | 35–170 |
| 717 | n-C10 (Appendix C) .......................................... | 51 | 24–195 | ........................ | 42–235 | 19–237 |
| 617 | n-C10-d22 ......................................................... | 70 | ns–298 | ns-ns | 44–227 | ns–504 |
| 706 | n-C12 (Appendix C) .......................................... | 74 | 35–369 | ........................ | 60–166 | 29–424 |
| 606 | n-C12-d26 ......................................................... | 53 | ns–331 | ns-ns | 41–242 | ns–408 |
| 518 | n-C14 (Appendix C)* ......................................... | 109 | ns–985 | ........................ | 37–268 | ns-ns |
| 719 | n-C16 (Appendix C) .......................................... | 33 | 80–162 | ........................ | 72–138 | 71–181 |
| 619 | n-C16-d34 ......................................................... | 46 | 37–162 | 18–308 | 54–186 | 28–202 |
| 520 | n-C18 (Appendix C)* ......................................... | 39 | 42–131 | ........................ | 40–249 | 35–167 |
| 721 | n-C20 (Appendix C) .......................................... | 59 | 53–263 | ........................ | 54–184 | 46–301 |
| 621 | n-C20-d42 ......................................................... | 34 | 34–172 | 19–306 | 62–162 | 29–198 |
| 522 | n-C22 (Appendix C)* ......................................... | 31 | 45–152 | ........................ | 40–249 | 39–195 |
| 723 | n-C24 (Appendix C) .......................................... | 11 | 80–139 | ........................ | 65–154 | 78–142 |
| 623 | n-C24-d50 ......................................................... | 28 | 27–211 | 15–376 | 50–199 | 25–229 |
| 524 | n-C26 (Appendix C)* ......................................... | 35 | 35–193 | ........................ | 26–392 | 31–212 |
| 525 | n-C28 (Appendix C)* ......................................... | 35 | 35–193 | ........................ | 26–392 | 31–212 |
| 726 | n-C30 (Appendix C) .......................................... | 32 | 61–200 | ........................ | 66–152 | 56–215 |
| 626 | n-C30-d62 ......................................................... | 41 | 27–242 | 13–479 | 24–423 | 23–274 |
| 528 | Carbazole (4c)* ................................................. | 38 | 36–165 | ........................ | 44–227 | 31–188 |
| 320 | 2-chloronaphthalene ......................................... | 100 | 46–357 | ........................ | 58–171 | 35–442 |
| 220 | 2-chloronaphthalene-d7 .................................... | 41 | 30–168 | 15–324 | 72–139 | 24–204 |
| 322 | 4-chloro-3-methylphenol ................................... | 37 | 76–131 | ........................ | 85–115 | 62–159 |
| 222 | 4-chloro-3-methylphenol-d2 .............................. | 111 | 30–174 | ns–613 | 68–147 | 14–314 |
| 324 | 2-chlorophenol .................................................. | 13 | 79–135 | ........................ | 78–129 | 76–138 |
| 224 | 2-chlorophenol-d4 ............................................. | 24 | 36–162 | 23–255 | 55–180 | 33–176 |
| 340 | 4-chlorophenyl phenyl ether ............................. | 42 | 75–166 | ........................ | 71–142 | 63–194 |
| 240 | 4-chlorophenyl phenyl ether-d5 ........................ | 52 | 40–161 | 19–325 | 57–175 | 29–212 |
| 376 | Chrysene ........................................................... | 51 | 59–186 | ........................ | 70–142 | 48–221 |
| 276 | Chrysene-d12 .................................................... | 69 | 33–219 | 13–512 | 24–411 | 23–290 |
| 713 | p-cymene (Appendix C) .................................... | 18 | 76–140 | ........................ | 79–127 | 72–147 |
| 613 | p-cymene-d14 ................................................... | 67 | ns–359 | ns-ns | 66–152 | ns–468 |
| 082 | Dibenzo(a,h)anthracene* .................................. | 55 | 23–299 | ........................ | 13–761 | 19–340 |
| 705 | Dibenzofuran (Appendix C) .............................. | 20 | 85–136 | ........................ | 73–136 | 79–146 |
| 605 | Dibenzofuran-d8 ................................................ | 31 | 47–136 | 28–220 | 66–150 | 39–160 |
| 704 | Dibenzothiophene (Synfuel) .............................. | 31 | 79–150 | ........................ | 72–140 | 70–168 |
| 604 | Dibenzothiophene-d8 ........................................ | 31 | 48–130 | 29–215 | 69–145 | 40–156 |
| 368 | Di-n-butyl phthalate ........................................... | 15 | 76–165 | ........................ | 71–142 | 74–169 |
| 268 | Di-n-butyl phthalate-d4 ...................................... | 23 | 23–195 | 13–346 | 52–192 | 22–209 |
| 325 | 1,2-dichlorobenzene .......................................... | 17 | 73–146 | ........................ | 74–135 | 70–152 |
| 225 | 1,2-dichlorobenzene-d4 .................................... | 35 | 14–212 | ns–494 | 61–164 | 11–247 |
| 326 | 1,3-dichlorobenzene .......................................... | 43 | 63–201 | ........................ | 65–154 | 55–225 |
| 226 | 1,3-dichlorobenzene-d4 .................................... | 48 | 13–203 | ns–550 | 52–192 | ns–260 |
| 327 | 1,4-dichlorobenzene .......................................... | 42 | 61–194 | ........................ | 62–161 | 53–219 |

#### Pt. 136, App. A, Meth. 1625

40 CFR Ch. I (7–1–17 Edition)

TABLE 8—ACCEPTANCE CRITERIA FOR PERFORMANCE TESTS—Continued

| EGD No. 1 | Compound | Acceptance criteria |
| --- | --- | --- |
|  |  | Initial precision and ac- curacy section 8.2.3 (g/L) | Labeled com- pound recov- ery sec. 8.3 and 14.2 P (percent) | Calibration verification sec. 12.5 (g/mL) | On-going accuracy sec. 11.6 R (g/L) |
|  |  | s | X |  |  |  |
| 227 | 1,4-dichlorobenzene-d4 .................................... | 48 | 15–193 | ns–474 | 65–153 | 11–245 |
| 328 | 3,3-dichlorobenzidine ....................................... | 26 | 68–174 | ........................ | 77–130 | 64–185 |
| 228 | 3,3-dichlorobenzidine-d6 .................................. | 80 | ns–562 | ns-ns | 18–558 | ns-ns |
| 331 | 2,4-dichlorophenol ............................................. | 12 | 85–131 | ........................ | 67–149 | 83–135 |
| 231 | 2,4-dichlorophenol-d3 ....................................... | 28 | 38–164 | 24–260 | 64–157 | 34–182 |
| 370 | Diethyl phthalate ............................................... | 44 | 75–196 | ........................ | 74–135 | 65–222 |
| 270 | Diethyl phthalate-d4 .......................................... | 78 | ns–260 | ns-ns | 47–211 | ns-ns |
| 334 | 2,4-dimethylphenol ............................................ | 13 | 62–153 | ........................ | 67–150 | 60–156 |
| 234 | 2,4-dimethylphenol-d3 ....................................... | 22 | 15–228 | ns–449 | 58–172 | 14–242 |
| 371 | Dimethyl phthalate ............................................ | 36 | 74–188 | ........................ | 73–137 | 67–207 |
| 271 | Dimethyl phthalate-d4 ....................................... | 108 | ns–640 | ns-ns | 50–201 | ns-ns |
| 359 | 2,4-dinitrophenol ............................................... | 18 | 72–134 | ........................ | 75–133 | 68–141 |
| 259 | 2,4-dinitrophenol-d3 .......................................... | 66 | 22–308 | ns-ns | 39–256 | 17–378 |
| 335 | 2,4-dinitrotoluene .............................................. | 18 | 75–158 | ........................ | 79–127 | 72–164 |
| 235 | 2,4-dinitrotoluene-d3 ......................................... | 37 | 22–245 | 10–514 | 53–187 | 19–275 |
| 336 | 2,6-dinitrotoluene .............................................. | 30 | 80–141 | ........................ | 55–183 | 70–159 |
| 236 | 2,6-dinitrotoluene-d3 ......................................... | 59 | 44–184 | 17–442 | 36–278 | 31–250 |
| 369 | Di-n-octyl phthalate ........................................... | 16 | 77–161 | ........................ | 71–140 | 74–166 |
| 269 | Di-n-octyl phthalate-d4 ...................................... | 46 | 12–383 | ns-ns | 21–467 | 10–433 |
| 707 | Diphenylamine (Appendix C) ............................ | 45 | 58–205 | ........................ | 57–176 | 51–231 |
| 607 | Diphenylamine-d10 ........................................... | 42 | 27–206 | 11–488 | 59–169 | 21–249 |
| 708 | Diphenyl ether (Appendix C) ............................ | 19 | 82–136 | ........................ | 83–120 | 77–144 |
| 608 | Diphenyl ether-d10 ............................................ | 37 | 36–155 | 19–281 | 77–129 | 29–186 |
| 337 | 1,2-diphenylhydrazine ....................................... | 73 | 49–308 | ........................ | 75–134 | 40–360 |
| 237 | 1,2-diphenylhydrazine-d10 ................................ | 35 | 31–173 | 17–316 | 58–174 | 26–200 |
| 339 | Fluoranthene ..................................................... | 33 | 71–177 | ........................ | 67–149 | 64–194 |
| 239 | Fluoranthene-d10 .............................................. | 35 | 36–161 | 20–278 | 47–215 | 30–187 |
| 380 | Fluorene ............................................................ | 29 | 81–132 | ........................ | 74–135 | 70–151 |
| 280 | Fluorene-d10 ..................................................... | 43 | 51–131 | 27–238 | 61–164 | 38–172 |
| 309 | Hexachlorobenzene .......................................... | 16 | 90–124 | ........................ | 78–128 | 85–132 |
| 209 | Hexachlorobenzene-13C6 ................................ | 81 | 36–228 | 13–595 | 38–265 | 23–321 |
| 352 | hexachlorobutadiene ......................................... | 56 | 51–251 | ........................ | 74–135 | 43–287 |
| 252 | hexachlorobutadiene-13C4 ............................... | 63 | ns–316 | ns-ns | 68–148 | ns–413 |
| 312 | hexachloroethane .............................................. | 227 | 21–ns | ........................ | 71–141 | 13–ns |
| 212 | hexachloroethane-13C1 .................................... | 77 | ns–400 | ns-ns | 47–212 | ns–563 |
| 353 | hexachlorocyclopentadiene ............................... | 15 | 69–144 | ........................ | 77–129 | 67–148 |
| 253 | hexachlorocyclopentadiene-13C4 ..................... | 60 | ns-ns | ns-ns | 47–211 | ns-ns |
| 083 | ideno(1,2,3-cd)pyrene* ...................................... | 55 | 23–299 | ........................ | 13–761 | 19–340 |
| 354 | isophorone ........................................................ | 25 | 76–156 | ........................ | 70–142 | 70–168 |
| 254 | isophorone-d8 ................................................... | 23 | 49–133 | 33–193 | 52–194 | 44–147 |
| 360 | 2-methyl-4,6-dinitrophenol ................................ | 19 | 77–133 | ........................ | 69–145 | 72–142 |
| 260 | 2-methyl-4,6-dinitrophenol-d2 ........................... | 64 | 36–247 | 16–527 | 56–177 | 28–307 |
| 355 | naphthalene ...................................................... | 20 | 80–139 | ........................ | 73–137 | 75–149 |
| 255 | naphthalene-d8 ................................................. | 39 | 28–157 | 14–305 | 71–141 | 22–192 |
| 702 | B-naphthylamine (Appendix C) ......................... | 49 | 10–ns | ........................ | 39–256 | ns-ns |
| 602 | B-naphthylamine-d7 .......................................... | 33 | ns-ns | ns-ns | 44–230 | ns-ns |
| 356 | nitrobenzene ..................................................... | 25 | 69–161 | ........................ | 85–115 | 65–169 |
| 256 | nitrobenzene-d5 ................................................ | 28 | 18–265 | ns-ns | 46–219 | 15–314 |
| 357 | 2-nitrophenol ..................................................... | 15 | 78–140 | ........................ | 77–129 | 75–145 |
| 257 | 2-nitrophenol-d4 ................................................ | 23 | 41–145 | 27–217 | 61–163 | 37–158 |
| 358 | 4-nitrophenol ..................................................... | 42 | 62–146 | ........................ | 55–183 | 51–175 |
| 258 | 4-nitrophenol-d4 ................................................ | 188 | 14–398 | ns-ns | 35–287 | ns-ns |
| 061 | N-nitrosodimethylamile* .................................... | 198 | 21–472 | ........................ | 40–249 | 12–807 |
| 063 | N-nitrosodi-n-proplyamine* ............................... | 198 | 21–472 | ........................ | 40–249 | 12–807 |
| 362 | N-nitrosodiphenylamine .................................... | 45 | 65–142 | ........................ | 68–148 | 53–173 |
| 262 | N-nitrosodiphenylamine-d6 ............................... | 37 | 54–126 | 26–256 | 59–170 | 40–166 |
| 364 | pentachlorophenol ............................................. | 21 | 76–140 | ........................ | 77–130 | 71–150 |
| 264 | pentachlorophenol-13C6 ................................... | 49 | 37–212 | 18–412 | 42–237 | 29–254 |
| 381 | phenanthrene .................................................... | 13 | 93–119 | ........................ | 75–133 | 87–126 |
| 281 | phenanthrene-d10 ............................................. | 40 | 45–130 | 24–241 | 67–149 | 34–168 |
| 365 | phenol ............................................................... | 36 | 77–127 | ........................ | 65–155 | 62–154 |
| 265 | phenol-d5 .......................................................... | 161 | 21–210 | ns-ns | 48–208 | ns-ns |
| 703 | a-picoline (Synfuel) ........................................... | 38 | 59–149 | ........................ | 60–165 | 50–174 |
| 603 | a-picoline-d7 ...................................................... | 138 | 11–380 | ns-ns | 31–324 | ns–608 |
| 384 | pyrene ............................................................... | 19 | 76–152 | ........................ | 76–132 | 72–159 |
| 284 | pyrene-d10 ........................................................ | 29 | 32–176 | 18–303 | 48–210 | 28–196 |
| 710 | styrene (Appendix C) ........................................ | 42 | 53–221 | ........................ | 65–153 | 48–244 |

#### Environmental Protection Agency	Pt. 136, App. A, Meth. 1625

TABLE 8—ACCEPTANCE CRITERIA FOR PERFORMANCE TESTS—Continued

| EGD No. 1 | Compound | Acceptance criteria |
| --- | --- | --- |
|  |  | Initial precision and ac- curacy section 8.2.3 (g/L) | Labeled com- pound recov- ery sec. 8.3 and 14.2 P (percent) | Calibration verification sec. 12.5 (g/mL) | On-going accuracy sec. 11.6 R (g/L) |
|  |  | s | X |  |  |  |
| 610 709 609 529 308 208 530 531 321 221 | styrene-d5 ......................................................... a-terpineol (Appendix C) ................................... a-terpineol-d3 .................................................... 1,2,3-trichlorobenzene (4c)* .............................. 1,2,4-trichlorobenzene ...................................... 1,2,4-trichlorobenzene-d3 ................................. 2,3,6-trichlorophenol (4c)* ................................. 2,4,5-trichlorophenol (4c)* ................................. 2,4,6-trichlorophenol ......................................... 2,4,6-trichlorophenol-d2 .................................... | 49 44 48 69 19 57 30 30 57 47 | ns–281 42–234 22–292 15–229 82–136 15–212 58–137 58–137 59–205 43–183 | ns-ns ........................ ns–672 ........................ ........................ ns–592 ........................ ........................ ........................ 21–363 | 44–228 54–186 20–502 60–167 78–128 61–163 56–180 56–180 81–123 69–144 | ns–348 38–258 18–339 11–297 77–144 10–282 51–153 51–153 48–244 34–226 |

1 Reference numbers beginning with 0, 1 or 5 indicate a pollutant quantified by the internal standard method; reference num- bers beginning with 2 or 6 indicate a labeled compound quantified by the internal standard method; reference numbers beginning with 3 or 7 indicate a pollutant quantified by isotope dilution.

* Measured by internal standard; specification derived from related compound. ns = no specification; limit is outside the range that can be measured reliably.

#### Pt. 136, App. A, Meth. 1625

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 1625

Pt. 136, App. A, Meth. 1625

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	Pt. 136, App. A, Meth. 1625

ATTACHMENT 1 TO METHOD 1625 INTRODUCTION

To     support     measurement     of     several

semivolatile pollutants, EPA  has  developed this attachment to EPA Method 1625B. 1 The modifications listed in this attachment are approved only for monitoring wastestreams from the Centralized Waste Treatment Point Source Category (40 CFR part 437) and the Landfills  Point  Source   Category   (40   CFR part 445). EPA Method 1625B (the Method) employs sample extraction with methylene chloride followed by analysis of the extract using capillary column gas chromatography- mass spectrometry  (GC/MS).  This  attach- ment addresses the addition  of  the semivolatile pollutants listed  in  Tables  1  and 2 to all applicable standard, stock,  and  spik- ing  solutions  utilized   for   the   determination of semivolatile organic compounds by EPA Method 1625B.

1.0    EPA METHOD 1625 REVISION B MODIFICATION     SUMMARY

The additional semivolatile organic com- pounds listed in Tables 1  and  2  are  added  to all applicable calibration, spiking, and other solutions utilized  in the  determination of semivolatile  compounds  by   EPA   Method 1625. The  instrument is  to be  calibrated with these compounds, and all procedures and quality control tests described in the Method must  be  performed.

2.0    SECTION MODIFICATIONS

NOTE: All section and figure numbers in this Attachment reference section and figure numbers in EPA Method 1625 Revision B un- less noted otherwise. Sections not listed here remain unchanged.

Section 6.7 The stock standard solutions de- scribed in this section are modified such that the analytes in Tables 1 and 2 of this attachment are required in addition to those  specified  in  the  Method.

Section 6.8 The labeled compound spiking solution in this section is modified to in- clude the labeled compounds listed in Ta- bles 5 and 6 of this attachment.

Section 6.9 The secondary standard is modi- fied to include the additional analytes listed in Tables 1 and 2 of this attach- ment.

1 EPA Method 1625 Revision  B, Semivolatile Organic Compounds by Isotope Dilution GC/MS, 40 CFR part 136, appendix A.

Section 6.12 The solutions for obtaining au- thentic mass spectra are to include all additional analytes  listed  in  Tables  1  and 2  of  this  attachment.

Section 6.13 The calibration solutions are modified to include the analytes listed in Tables 1 and 2 and the labeled compounds listed in Tables 5 and 6 of this attach- ment.

Section 6.14 The precision and recovery standard is modified to include the analytes listed in Tables 1 and 2 and the labeled compounds listed  in  Tables  5  and 6  of  this  attachment.

Section 6.15 The solutions containing the additional  analytes  listed  in  Tables  1  and

2  of  this  attachment  are  to  be  analyzed for   stability.

Section 7.2.1 This section is modified to  in- clude the  analytes  listed  in  Tables  1  and 2 and the labeled compounds listed in Ta- bles 5 and 6 of this attachment.

Section 7.4.5 This section is modified to  in- clude the  analytes  listed  in  Tables  1  and 2 and the labeled compounds listed in Ta- bles 5 and 6 in the calibration.

Section 8.2 The  initial  precision  and  recov- ery (IPR) requirements are modified to include  the  analytes  listed  in  Tables  1 and 2 and the labeled compounds listed in Tables 5 and 6 of this attachment. Addi- tional IPR performance criteria are sup- plied  in  Table  7  of  this  attachment.

Section 8.3 The labeled compounds listed in Tables 3 and 4 of  this  attachment  are  to be included  in the method performance tests. Additional method performance criteria are supplied in Table 7 of this at- tachment.

Section 8.5.2 The  acceptance  criteria  for blanks includes the analytes listed in Ta- bles 1 and 2 of this attachment.

Section 10.1.2 The labeled compound solu- tion must include the labeled compounds listed in Tables 5 and 6 of this attach- ment.

Section 10.1.3 The precision and recovery standard must include the  analytes  list- ed in Tables 1 and 2 and the labeled com- pounds listed in Tables 5 and 6 of this at- tachment.

Section 12.5 Additional QC requirements for calibration verification are  supplied  in Table  7  of  this  attachment.

Section 12.7 Additional QC requirements for ongoing precision and recovery are sup- plied  in  Table  7  of  this  attachment.

#### Pt. 136, App. A, Meth. 1625

40 CFR Ch. I (7–1–17 Edition)

TABLE 1—BASE/NEUTRAL EXTRACTABLE COMPOUNDS

| Compound | Pollutant |
| --- | --- |
|  | CAS Registry | EPA-EGD |
| acetophenone 1 .......................................................................................................................................... | 98–86–2 | 758 |
| aniline 2 ...................................................................................................................................................... | 62–53–3 | 757 |
| -2,3-dichloroaniline 1 .................................................................................................................................. | 608–27–5 | 578 |
| -o-cresol 1 .................................................................................................................................................. | 95–48–7 | 771 |
| pyridine 2 .................................................................................................................................................... | 110–86–1 | 1330 |

CAS = Chemical Abstracts Registry. EGD = Effluent Guidelines Division.

1 Analysis of this pollutant is approved only for the Centralized Waste Treatment industry.

2 Analysis of this pollutant is approved only for the Centralized Waste Treatment and Landfills industries.

TABLE 2—ACID EXTRACTABLE COMPOUNDS

| Compound | Pollutant |
| --- | --- |
|  | CAS Registry | EPA-EGD |
| p-cresol 1 .................................................................................................................................................... | 106–44–5 | 1744 |

CAS = Chemical Abstracts Registry. EGD = Effluent Guidelines Division.

1 Analysis of this pollutant is approved only for the Centralized Waste Treatment and Landfills industries.

TABLE 3—GAS CHROMATOGRAPHY 1 OF BASE/NEUTRAL EXTRACTABLE COMPOUNDS

| EGD No. | Compound | Retention time 2 | Minimum level 3 (g/L) |
| --- | --- | --- | --- |
|  |  | Mean (sec) | EGD Ref | Relative |  |
| 758 ....................... | acetophenone 4 ................................... | 818 | 658 | 1.003–1.005 | 10 |
| 757 ....................... | aniline 5 ................................................ | 694 | 657 | 0.994–1.023 | 10 |
| 578 ....................... | 2,3-dichloroaniline 4 ............................. | 1160 | 164 | 1.003–1.007 | 10 |
| 771 ....................... | o-cresol 4 ............................................. | 814 | 671 | 1.005–1.009 | 10 |
| 1330 ..................... | pyridine 5 .............................................. | 378 | 1230 | 1.005–1.011 | 10 |

EGD = Effluent Guidelines Division.

1 The data presented in this table were obtained under the chromatographic conditions given in the footnote to Table 3 of EPA Method 1625B.

2 Retention times are approximate and are intended to be consistent with the retention times for the analytes in EPA Method 1625B.

3 See the definition in footnote 2 to Table 3 of EPA Method 1625B.

4 Analysis of this pollutant is approved only for the Centralized Waste Treatment industry.

5 Analysis of this pollutant is approved only for the Centralized Waste Treatment and Landfills industries.

TABLE 4—GAS CHROMATOGRAPHY 1 OF ACID EXTRACTABLE COMPOUNDS

| EGD No. | Compound | Retention time 2 | Minimum level (/L) 3 |
| --- | --- | --- | --- |
|  |  | Mean (sec) | EGD Ref | Relative |  |
| 1744 ..................... | p-cresol 4 ............................................. | 834 | 1644 | 1.004–1.008 | 20 |

EGD = Effluent Guidelines Division.

1 The data presented in this table were obtained under the chromatographic conditions given in the footnote to Table 4 of EPA Method 1625B.

2 Retention times are approximate and are intended to be consistent with the retention times for the analytes in EPA Method 1625B.

3 See the definition in footnote 2 to Table 4 of EPA Method 1625B.

4 Analysis of this pollutant is approved only for the Centralized Waste Treatment and Landfills industries.

TABLE 5—BASE/NEUTRAL EXTRACTABLE COMPOUND CHARACTERISTIC M/Z’S

| Compound | Labeled Ana- log | Primary m/z 1 |
| --- | --- | --- |
| acetophenone 2 .................................................................................................................................. | d5 | 105/110 |
| aniline 3 .............................................................................................................................................. | d7 | 93/100 |
| o-cresol 2 ............................................................................................................................................ | d7 | 108/116 |
| 2,3-dichloroaniline 2 ........................................................................................................................... | n/a | 161 |
| pyridine 3 ............................................................................................................................................ | d5 | 79/84 |

m/z = mass to charge ratio.

#### Environmental Protection Agency	Pt. 136, App. B

1 Native/labeled.

2 Analysis of this pollutant is approved only for the Centralized Waste Treatment industry.

3 Analysis of this pollutant is approved only for the Centralized Waste Treatment and Landfills industries.

TABLE 6—ACID EXTRACTABLE COMPOUND CHARACTERISTIC M/Z’S

| Compound | Labeled Ana- log | Primary m/z 1 |
| --- | --- | --- |
| p-cresol 2 ............................................................................................................................................ | d7 | 108/116 |

m/z = mass to charge ratio.

1 Native/labeled.

2 Analysis of this pollutant is approved only for the Centralized Waste Treatment and Landfills industries.

TABLE 7—ACCEPTANCE CRITERIA FOR PERFORMANCE TESTS

| EGD No. | Compound | Acceptance criteria | Calibration verification sec. 12.5 g/mL) | On-going accuracy sec. 12.7 R (g/L) |
| --- | --- | --- | --- | --- |
|  |  | Initial precision and accu- racy section 8.2 (g/L) | Labeled compound recovery sec. 8.3 and 14.2 P (percent) |  |  |
|  |  | s (g/L) | X |  |  |  |
| 758 ....................... 658 ....................... 757 ....................... 657 ....................... 771 ....................... 671 ....................... 1744 ..................... 1644 ..................... 578 ....................... 1330 ..................... 1230 ..................... | acetophenone 1 ........................... acetophenone-d 5 1 ...................... aniline 2 ....................................... aniline-d 7 2 .................................. o-cresol 1 ..................................... o-cresol-d 7 1 ................................ p-cresol 2 ..................................... p-cresol-d7 2 ................................ 2,3-dichloroaniline 1 ..................... pyridine 2 ..................................... pyridine-d 5 2 ................................ | 34 51 32 71 40 23 59 22 13 28 ns | 44–167 23–254 30–171 15–278 31–226 30–146 54–140 11–618 40–160 10–421 7–392 | .................... 45–162 .................... 33–154 .................... 35–196 .................... 37–203 .................... .................... 19–238 | 85–115 85–115 85–115 85–115 85–115 85–115 85–115 85–115 85–115 83–117 85–115 | 45–162 22–264 33–154 12–344 35–196 31–142 37–203 16–415 44–144 18–238 4–621 |

s = Standard deviation of four recovery measurements. X = Average recovery for four recovery measurements. EGD = Effluent Guidelines Division.

ns = no specification; limit is outside the range that can be measured reliably.

1 Analysis of this pollutant is approved only for the Centralized Waste Treatment industry.

2 Analysis of this pollutant is approved only for the Centralized Waste Treatment and Landfills industries.

[49 FR 43261, Oct. 26, 1984; 50 FR 692, 695, Jan. 4, 1985, as amended at 51 FR 23702, June 30, 1986;

62 FR 48405, Sept. 15, 1997; 65 FR 3044, Jan. 19, 2000; 65 FR 81295, 81298, Dec. 22, 2000]

APPENDIX B TO PART 136—DEFINITION AND PROCEDURE FOR THE DETER- MINATION OF THE METHOD DETEC- TION LIMIT—REVISION 1.11

Definition

The method detection limit (MDL) is de- fined as the minimum concentration of a substance that can be measured and reported with 99% confidence that the analyte con- centration is greater than zero and is deter- mined from analysis of a sample in a given matrix containing the analyte.

Scope and Application

This procedure is designed for applicability to a wide variety of sample types ranging from reagent (blank) water containing analyte to wastewater containing analyte. The MDL for an analytical procedure may vary as a function of sample type. The proce- dure requires a complete, specific, and well defined analytical method. It is essential that all sample processing steps of the ana-

lytical method be included in the determina- tion of the method detection limit.

The MDL obtained by this procedure is used to judge the significance of a single measurement of a future sample.

The MDL procedure was designed for appli- cability to a broad variety of physical and chemical methods. To accomplish this, the procedure was made device- or instrument- independent.

Procedure

- Make an estimate of the detection limit using one of the following:

- The concentration value that cor- responds to an instrument signal/noise in the range of 2.5 to 5.

- The concentration equivalent of three times the standard deviation of replicate in- strumental measurements of the analyte in reagent water.

- That region of the standard curve where there is a significant change in sensitivity, i.e., a break in the slope of the standard curve.

#### Pt. 136, App. B

- Instrumental  limitations.

It is recognized that the experience of the analyst is important to this process. How- ever, the analyst must include the above considerations in the initial estimate of the detection   limit.

- Prepare reagent (blank) water that is as free of analyte as possible. Reagent or inter- ference free water is defined as a water sam- ple in which analyte and interferent con- centrations are not detected at the method detection limit of each analyte of interest. Interferences are defined as systematic er- rors in the measured analytical signal of an established procedure caused by the presence of interfering species (interferent). The interferent concentration is presupposed to be normally distributed in representative samples of a given matrix.

- (a) If the MDL is to be determined in re- agent (blank)  water,  prepare  a  laboratory standard (analyte in reagent water) at a con- centration which is at least equal  to  or  in the same concentration range as the esti- mated method detection limit. (Recommend between 1 and 5 times the estimated method detection limit.) Proceed to Step 4.

- If the MDL is to be determined in an- other sample matrix, analyze the sample. If the measured level of the analyte is in the recommended range of one to five times the estimated detection limit, proceed to Step 4. If  the  measured  level  of  analyte  is  less than  the  estimated  detection  limit,  add  a known amount of analyte to bring the level of analyte between one and five times the es-

timated detection limit.

If the measured level of analyte is greater than five times the estimated  detection limit, there are two options.

  - Obtain another sample with a lower level of analyte in the same matrix if pos- sible.

  - The sample may be used as is for deter- mining the method detection limit if the analyte level does not exceed 10 times the MDL of the analyte in reagent water. The variance of the analytical method changes as the analyte concentration increases from the MDL,   hence   the   MDL   determined   under

#### 40 CFR Ch. I (7–1–17 Edition)

these circumstances may not truly reflect method variance at lower analyte concentra- tions.

- (a) Take a minimum of seven aliquots of the sample to be used to calculate the meth- od detection limit and process each through the entire analytical method. Make all com- putations according to the defined method with final results in the method reporting units. If a blank measurement is required to calculate the measured level of analyte, ob- tain a separate blank measurement for each sample aliquot analyzed. The average blank measurement is subtracted from the respec- tive sample measurements.

- It may be economically and technically desirable to evaluate the estimated method detection limit before proceeding with 4a. This will: (1) Prevent repeating this entire procedure when the costs of analyses are high and (2) insure that the procedure is being conducted at the correct concentra- tion. It is quite possible that an inflated MDL will be calculated from data obtained at many times the real MDL even though the level of analyte is less than five times the calculated method detection limit. To insure that the estimate of the method detection limit is a  good estimate,  it is  necessary to determine that a lower concentration of analyte will  not result in  a significantly lower method detection limit. Take two aliquots of the sample to be used to calculate the method detection limit and process each through the entire method, including blank measurements as described above in 4a. Evaluate these data:

  - If these measurements indicate the sample is in desirable range for determina- tion of the MDL,  take  five  additional aliquots and proceed. Use all seven measure- ments for calculation of the MDL.

  - If these measurements indicate the sample is not in correct range,  reestimate the MDL, obtain new sample as in 3 and re- peat either 4a or 4b.

- Calculate the variance (S2) and standard deviation (S) of the replicate measurements, as follows:

2

⎡n     2     ⎛n        ⎞⎤

⎢xi ⎜Xi ⎟⎥

S2 1  ⎢i 1	⎝i 1       ⎠⎥

⎢

⎥

n 1 ⎢	n	⎥

⎢	⎥

⎣	⎦

1

S S2 2

where:	X; i = 1 to n,  are  the  analytical  results  in the final method reporting units ob- tained from the n sample aliquots and S

#### Environmental Protection Agency	Pt. 136, App. B

refers to the sum of the X values from i

= l to n.

- (a) Compute the MDL as follows: MDL = tn-1,1-(S)

where:

MDL = the method detection limit

tn-1,1-= the students’ t value appro- priate for a 99% confidence level and a standard deviation estimate with n-1 de- grees of freedom. See Table.

S = standard deviation of the replicate anal- yses.

(b) The 95% confidence interval estimates for the MDL derived in 6a are computed ac- cording  to  the  following  equations  derived

- Optional iterative procedure to verify the reasonableness of the estimate of the MDL and subsequent MDL determinations.

- If this is the initial attempt to compute MDL based on the estimate of MDL formu- lated in Step 1, take the MDL as calculated in Step 6, spike the matrix at this calculated MDL and proceed through the procedure starting with Step 4.

- If this is the second or later iteration of the MDL calculation, use S2 from the cur- rent MDL calculation and S2  from the pre- vious MDL calculation to compute the F- ratio. The F-ratio is calculated by sub- stituting  the  larger  S2   into  the  numerator

from  percentiles  of  the  chi  square  over  de-	S2	2

grees of freedom distribution (c2/df). LCL = 0.64 MDL

UCL = 2.20 MDL

where: LCL and UCL are the lower and upper 95% confidence limits respectively based on seven aliquots.

A and the other into the denominator S B.

The computed F-ratio is then compared with the F-ratio found in the table which is 3.05 as

follows:  if  S2   /S2   <3.05,  then  compute  the

A      B

pooled  standard  deviation  by  the  following equation:

1

⎡6S2  6S2 ⎤2

S		A	B

pooled	⎢	⎥

## ⎣	12	⎦

if S2   /S2   >3.05, respike at the most recent

A        B	TABLES OF STUDENTS’ T VALUES AT THE 99

calculated MDL and process the samples

through the procedure starting with Step

4. If the most recent calculated MDL does not permit qualitative identifica- tion when samples are spiked at that level, report the MDL as a concentration between the current and previous MDL which permits qualitative identification.

- Use the Spooled as calculated in 7b to compute The final MDL according to the fol- lowing equation:

MDL = 2.681 (Spooled)

where 2.681 is equal to t12,1¥.99.

- The 95% confidence limits for MDL de- rived in 7c are computed according to the following equations derived from precentiles of the chi squared over degrees of freedom distribution.

LCL = 0.72 MDL UCL = 1.65 MDL

where LCL and UCL are the lower and upper 95% confidence limits respectively based on 14 aliquots.

| Number of replicates | Degrees of free- dom (n-1) | tcn-1,.99) |
| --- | --- | --- |
| 7 ..................................................... 8 ..................................................... | 6 7 | 3.143 2.998 |

TABLES OF STUDENTS’ T VALUES AT THE 99 PERCENT CONFIDENCE LEVEL

PERCENT CONFIDENCE LEVEL—Continued

| Number of replicates | Degrees of free- dom (n-1) | tcn-1,.99) |
| --- | --- | --- |
| 9 ..................................................... | 8 | 2.896 |
| 10 ................................................... | 9 | 2.821 |
| 11 ................................................... | 10 | 2.764 |
| 16 ................................................... | 15 | 2.602 |
| 21 ................................................... | 20 | 2.528 |
| 26 ................................................... | 25 | 2.485 |
| 31 ................................................... | 30 | 2.457 |
| 61 ................................................... | 60 | 2.390 |
| 00 ................................................... | 00 | 2.326 |

Reporting

The analytical method used must be spe- cifically identified by number or title ald the MDL for each analyte expressed in the ap- propriate method reporting units. If the ana- lytical method permits options which affect the method detection limit, these conditions must be specified with the MDL value. The sample matrix used to determine the MDL must also be identified with MDL value. Re- port the mean  analyte level with  the MDL and indicate if the MDL procedure was iterated. If a laboratory standard or a sam- ple that contained a known amount analyte was used for this determination, also report the mean recovery.

If the level of analyte in the sample was below  the  determined  MDL  or  exceeds  10

#### Pt. 136, App. C

times  the  MDL  of  the  analyte  in  reagent water, do not report a value for the MDL.

[49 FR 43430, Oct. 26, 1984; 50 FR 694, 696, Jan.

4, 1985, as amended at 51 FR 23703, June 30,

1986]

APPENDIX C TO PART 136—DETERMINA- TION OF METALS AND TRACE ELE- MENTS IN WATER AND WASTES BY IN- DUCTIVELY COUPLED  PLASMA-ATOM- IC EMISSION SPECTROMETRY METHOD 200.7

1.0   Scope and Application

  - Inductively coupled plasma-atomic emission spectrometry (ICP–AES) is used to determine metals and some nonmetals in so- lution. This method is a consolidation of ex- isting methods for water, wastewater, and solid wastes.1–4 (For analysis of petroleum products see References 5 and 6,  Section 16.0). This method is applicable to the fol- lowing  analytes:

| Analyte | Chemical abstract services registry number (CASRN) |
| --- | --- |
| Aluminum (Al) .................................... | 7429–90–5 |
| Antimony (Sb) .................................... | 7440–36–0 |
| Arsenic (As) ....................................... | 7440–38–2 |
| Barium (Ba) ....................................... | 7440–39–3 |
| Beryllium (Be) .................................... | 7440–41–7 |
| Boron (B) ........................................... | 7440–42–8 |
| Cadmium (Cd) ................................... | 7440–43–9 |
| Calcium (Ca) ...................................... | 7440–70–2 |
| Cerium a (Cr) ...................................... | 7440–45–1 |
| Chromium (Cr) ................................... | 7440–47–3 |
| Cobalt (Co) ........................................ | 7440–48–4 |
| Copper (Cu) ....................................... | 7440–50–8 |
| Iron (Fe) ............................................. | 7439–89–6 |
| Lead (Pb) ........................................... | 7439–92–1 |
| Lithium (Li) ......................................... | 7439–93–2 |
| Magnesium (Mg) ................................ | 7439–95–4 |
| Manganese (Mn) ............................... | 7439–96–5 |
| Mercury (Hg) ...................................... | 7439–97–6 |
| Molybdenum (Mo) .............................. | 7439–98–7 |
| Nickel (Ni) .......................................... | 7440–02–0 |
| Phosphorus (P) .................................. | 7723–14–0 |
| Potassium (K) .................................... | 7440–09–7 |
| Selenium (Se) .................................... | 7782–49–2 |
| Silica b (Si02) ...................................... | 7631–86–9 |
| Silver (Ag) .......................................... | 7440–22–4 |
| Sodium (Na) ...................................... | 7440–23–5 |
| Strontium (Sr) .................................... | 7440–24–6 |
| Thallium (Tl) ....................................... | 7440–28–0 |
| Tin (Sn) .............................................. | 7440–31–5 |
| Titanium (Ti) ...................................... | 7440–32–6 |
| Vanadium (V) ..................................... | 7440–62–2 |
| Zinc (Zn) ............................................ | 7440–66–6 |

a Cerium has been included as method analyte for correc- tion of potential interelement spectral interference.

b This method is not suitable for the determination of silica in solids.

  - For reference where this method is ap- proved for use in compliance monitoring pro- grams [e.g.,  Clean  Water  Act  (NPDES)  or Safe Drinking Water Act  (SDWA)]  consult both the appropriate sections of the Code of Federal  Regulation  (40  CFR  Part  136  Table

#### 40 CFR Ch. I (7–1–17 Edition)

1B for NPDES, and Part 141 § 141.23 for drink- ing water), and the latest FEDERAL REGISTER announcements.

  - ICP–AES can be used to determine dis- solved analytes in aqueous samples after suitable filtration and acid preservation. To reduce potential interferences, dissolved sol- ids should be <0.2% (w/v) (Section 4.2).

  - With the  exception  of  silver,  where this method is approved for the determina- tion of certain metal and metalloid contami- nants in drinking water, samples may be analyzed directly by pneumatic nebulization without acid digestion if the sample has been properly preserved with acid and has tur- bidity of <1 NTU at the time of  analysis. This total recoverable determination proce- dure is referred to as ‘‘direct analysis’’. How- ever, in the determination of some primary drinking water metal contaminants, preconcentration of the sample may be re- quired prior to analysis in order to meet drinking water acceptance performance cri- teria (Sections 11.2.2 through 11.2.7).

  - For the determination of total recov- erable analytes in aqueous and solid samples a digestion/extraction is required prior to analysis when  the  elements  are  not  in  solu- tion (e.g., soils, sludges, sediments and aque- ous samples  that  may  contain  particulate and suspended solids). Aqueous samples con- taining suspended or particulate material 1% (w/v) should be extracted as a solid type sam- ple.

  - When determining boron and silica in aqueous samples, only plastic, PTFE or quartz labware should be used from time of sample collection to completion of analysis. For accurate determination of boron in solid samples only quartz or PTFE beakers should be used during acid extraction with imme- diate transfer of an extract aliquot to a plas- tic centrifuge tube following dilution of the extract to volume. When possible, borosilicate glass should be avoided to pre- vent contamination of these analytes.

  - Silver is only slightly soluble in the presence of chloride unless there is a suffi- cient chloride concentration to form the soluble chloride complex. Therefore, low re- coveries of silver may occur in samples, for- tified sample matrices and even fortified blanks if determined as a dissolved analyte or by ‘‘direct analysis’’ where the sample has not been processed using the total recover- able mixed acid digestion. For this reason it is recommended that samples be digested prior to the determination of silver. The total recoverable sample digestion procedure given in this method is suitable for the de- termination of silver in aqueous samples containing concentrations up to 0.1 mg/L. For the analysis of wastewater samples con- taining higher concentrations of silver, suc- ceeding smaller volume, well mixed aliquots

#### Environmental Protection Agency	Pt. 136, App. C

should be prepared until the analysis solu- tion contains <0.1 mg/L silver. The extrac- tion of solid samples containing concentra- tions of silver >50 mg/kg should be treated in a similar manner. Also, the extraction of tin from solid samples should be prepared again using aliquots <1 g when determined sample concentrations exceed 1%.

  - The total recoverable sample digestion procedure given in this method will solu- bilize and hold in solution only minimal con- centrations of barium in the presence of free sulfate. For the analysis of barium in sam- ples having varying and unknown concentra- tions of sulfate, analysis should be com- pleted as soon as possible after sample prepa- ration.

  - The total recoverable sample digestion procedure given in this method is not suit- able for the determination of volatile organo-mercury compounds. However, if di- gestion is not required (turbidity <1  NTU), the combined concentrations of  inorganic and organo-mercury in solution can be deter- mined by ‘‘direct analysis’’ pneumatic nebulization provided the sample solution is adjusted to contain the same mixed acid (HNO3 + HCl) matrix as the total recoverable calibration standards and blank solutions.

  - Detection limits and linear ranges for the elements will vary with the wavelength selected, the spectrometer, and the matrices. Table 1 provides estimated instrument detec- tion limits for the listed wavelengths.7 How- ever, actual method detection limits and lin- ear working ranges will be dependent on the sample matrix, instrumentation, and  se- lected operating conditions.

  - Users of the method data should state the data-quality objectives prior to analysis. Users of the method must document and have on file the required initial demonstra- tion performance data described in Section

9.2 prior to using the method for analysis.

2.0   Summary of Method

  - An aliquot of a well mixed, homo- geneous aqueous or solid sample is accu- rately weighed or measured for sample proc- essing. For total recoverable analysis of a solid or an aqueous sample containing undissolved material, analytes are first solu- bilized by gentle refluxing with nitric and hydrochloric acids. After cooling, the sample is made up to volume, is mixed and centrifuged or allowed to settle overnight prior to analysis. For the determination of dissolved analytes in a filtered aqueous sam- ple aliquot, or for the ‘‘direct analysis’’ total recoverable determination of analytes in drinking water where sample turbidity is <1 NTU, the sample is made ready for analysis by the appropriate addition of nitric acid, and then diluted to a predetermined volume and mixed before analysis.

  - The analysis described in this method involves  multielemental  determinations  by

ICP–AES using sequential or simultaneous instruments. The instruments measure  char- acteristic atomic-line emission spectra by optical spectrometry. Samples are nebulized and the resulting aerosol is transported  to the plasma torch. Element specific emission spectra are produced by a radio-frequency in- ductively coupled plasma. The spectra are dispersed by a grating spectrometer, and the intensities of the line spectra are monitored at specific wavelengths by a photosensitive device. Photocurrents from the photosensi- tive device are processed and controlled by a computer system. A background correction technique is required to compensate for vari- able background contribution to the deter- mination of the analytes. Background  must be measured adjacent to the analyte wave- length during analysis. Various interferences must be considered and addressed appro- priately as discussed in Sections 4.0, 7.0, 9.0,

10.0, and 11.0.

3.0   Definitions

  - Calibration Blank—A volume of rea- gent water acidified with the same acid ma- trix as in the calibration standards. The cali- bration blank is a zero standard and is used to calibrate the ICP instrument (Section 7.10.1).

  - Calibration Standard (CAL)—A solu- tion prepared from the dilution of stock standard solutions. The CAL solutions are used to calibrate the instrument response with respect to analyte concentration (Sec- tion 7.9).

  - Dissolved Analyte—The concentration of analyte in an aqueous sample that will pass through a 0.45 m membrane filter as- sembly prior to sample acidification (Section 11.1).

  - Field Reagent Blank (FRB)—An ali- quot of reagent water or other blank matrix that is placed in a sample container in the laboratory and treated as a sample in all re- spects, including shipment to the sampling site, exposure to the sampling site condi- tions, storage, preservation, and all analyt- ical procedures. The purpose of the FRB is to determine if method analytes or other inter- ferences are present in the field environment (Section 8.5).

  - Instrument Detection  Limit  (IDL)— The concentration equivalent to the analyte signal which is equal to three times the standard deviation of a series of 10 replicate measurements of the calibration blank sig- nal at the same wavelength (Table 1.).

  - Instrument Performance Check  (IPC) Solution—A solution of method analytes, used to evaluate the performance of the in- strument system with respect to a  defined set of method criteria (Sections 7.11  and 9.3.4).

#### Pt. 136, App. C

  - Internal Standard—Pure analyte(s) added to a sample, extract, or standard solu- tion in known amount(s) and used to meas- ure the relative responses of other method analytes that are components of the same sample or solution. The internal  standard must be an analyte that is not a sample com- ponent (Section 11.5).

  - Laboratory Duplicates (LD1 and LD2)—Two aliquots of the same sample taken in the laboratory and analyzed sepa- rately with identical procedures. Analyses of LD1 and LD2 indicate precision associated with laboratory procedures, but not with sample collection, preservation, or storage procedures.

  - Laboratory Fortified Blank (LFB)—An aliquot of LRB to which known quantities of the method analytes are added in the labora- tory. The LFB is analyzed exactly like a sample, and its purpose is to determine whether the methodology is in control and whether the laboratory is capable of making accurate and precise measurements (Sec- tions 7.10.3 and 9.3.2).

  - Laboratory Fortified Sample Matrix (LFM)—An aliquot of an environmental sam- ple to which known quantities of the method analytes are added in the laboratory. The LFM is analyzed exactly like a sample, and its purpose is to determine whether the sam- ple matrix contributes bias to the analytical results. The background concentrations of the analytes in the sample matrix must be determined in a separate aliquot and the measured values in the LFM corrected for background concentrations (Section 9.4).

  - Laboratory Reagent  Blank  (LRB)— An aliquot of reagent water or other blank matrices that are treated exactly as  a  sam- ple including exposure to all glassware, equipment, solvents, reagents, and internal standards that are used with other samples. The LRB  is used  to determine  if method analytes or other interferences  are  present in the laboratory environment, reagents, or apparatus (Sections 7.10.2 and 9.3.1).

  - Linear Dynamic Range (LDR)—The concentration range over which the instru- ment response to an analyte is linear (Sec- tion 9.2.2).

  - Method Detection Limit (MDL)—The minimum concentration of an analyte that can be identified, measured, and reported with 99% confidence that the analyte con- centration is greater than zero (Section 9.2.4 and Table 4.).

  - Plasma Solution—A solution that is used to determine the optimum height above the work coil for viewing the plasma (Sec- tions 7.15 and 10.2.3).

  - Quality Control Sample (QCS)—A so- lution of method analytes of known con- centrations which is used to fortify an ali- quot of LRB or sample matrix. The QCS is obtained from a source external to the lab- oratory and different from the source of cali-

#### 40 CFR Ch. I (7–1–17 Edition)

bration standards. It is used to check either laboratory or instrument performance (Sec- tions 7.12 and 9.2.3).

  - Solid Sample—For the purpose of this method, a sample taken from material clas- sified as soil, sediment or sludge.

  - Spectral Interference Check (SIC) So- lution—A solution of selected method analytes of higher concentrations which is used to evaluate the procedural routine for correcting known interelement spectral interferences with respect to a defined set of method criteria (Sections 7.13, 7.14 and 9.3.5).

  - Standard Addition—The addition of a known amount of analyte to the sample in order to determine the relative response of the detector to an analyte within the sample matrix. The relative response is then used to assess either an operative matrix effect or the sample analyte concentration (Sections

9.5.1 and 11.5).

  - Stock Standard Solution—A con- centrated solution containing one or more method analytes prepared in the laboratory using assayed reference materials or pur- chased from a reputable commercial source (Section 7.8).

  - Total Recoverable Analyte—The con- centration of analyte determined either by ‘‘direct analysis’’ of an unfiltered acid pre- served drinking water sample with turbidity of <1 NTU (Section 11.2.1), or by analysis of the solution extract of a solid sample or an unfiltered aqueous sample following diges- tion by refluxing with hot dilute mineral acid(s) as specified in the method (Sections 11.2 and 11.3).

  - Water Sample—For the  purpose  of this method, a sample taken from one of the following sources: drinking, surface, ground, storm runoff, industrial or domestic waste- water.

4.0  Interferences

  - Spectral interferences are caused by background emission from continuous or re- combination phenomena,  stray  light  from the line emission of high concentration ele- ments, overlap of a spectral line from an- other element, or unresolved overlap of mo- lecular band spectra.

    - Background emission and stray  light can usually be compensated for by sub- tracting the background emission  deter- mined by measurement(s) adjacent to the analyte wavelength peak. Spectral scans of samples or single element solutions in the analyte regions may indicate not only when alternate wavelengths are desirable  because of severe spectral interference, but also will show whether the most appropriate estimate of the background emission is provided by an interpolation from measurements on both sides of the wavelength peak or by the meas- ured emission on one side or the other. The location(s) selected for the measurement of background  intensity  will  be  determined  by

#### Environmental Protection Agency	Pt. 136, App. C

the complexity of the spectrum adjacent to the wavelength peak. The location(s) used for routine measurement must be free of off- line spectral interference (interelement or molecular) or adequately corrected to reflect the same change in background intensity as occurs at the wavelength peak.

    - Spectral overlaps may be avoided by using an alternate wavelength or can be compensated for by equations that correct for interelement contributions, which in- volves measuring the interfering elements. Some potential on-line spectral interferences observed for the recommended wavelengths are given in Table 2. When operative and un- corrected, these interferences will produce false-positive determinations and be re- ported as analyte concentrations. The inter- ferences listed are only those that occur be- tween method analytes. Only  interferences of a direct overlap nature that were observed with a single instrument having a working resolution of 0.035 nm are listed. More exten- sive information on interferant effects at various wavelengths and resolutions is avail- able in Boumans’ Tables.8 Users may apply interelement correction factors determined on their instruments within tested con- centration ranges to compensate (off-line or on-line) for the effects of interfering ele- ments.

    - When interelement corrections are applied, there is a need to verify their accu- racy by analyzing  spectral  interference check solutions as described in Section 7.13. Interelement corrections will vary for  the same emission line among instruments be- cause of differences in resolution, as deter- mined by the grating plus the entrance  and exit slit widths, and by the order of disper- sion. Interelement corrections will also vary depending upon the choice of background correction points. Selecting a background correction point where an interfering emis- sion line may appear should be avoided when practical. Interelement corrections that con- stitute a major portion of an emission signal may not yield accurate data. Users  should not forget that some samples may contain uncommon elements  that  could  contribute spectral  interferences.7 8

    - The interference effects must be evaluated for each individual instrument whether configured as a sequential or simul- taneous instrument. For each instrument, intensities will vary not only with optical resolution but also with operating conditions (such as power, viewing height and argon flow rate). When using the recommended wavelengths given in Table 1, the analyst is required to determine and document for each wavelength the effect from the known inter- ferences given in Table 2, and to utilize a computer routine for their automatic correc- tion on all analyses. To determine the appro- priate location for off-line background cor- rection,  the  user  must  scan  the  area  on  ei-

ther side adjacent to the wavelength and record the apparent emission intensity from all other method analytes. This spectral in- formation must be documented and kept on file. The location selected for background correction must be either free of off-line interelement spectral interference or a com- puter routine must be used for their auto- matic correction on all determinations. If a wavelength other than the recommended wavelength is used, the user must determine and document both the on-line and off-line spectral interference effect from all method analytes and provide for their automatic cor- rection on all analyses. Tests to determine the spectral interference must be done using analyte concentrations that will adequately describe the interference. Normally, 100 mg/ L single element solutions are sufficient, however, for analytes such as iron that may be found at high concentration a more appro- priate test would be to use a concentration near the upper LDR limit. See Section 10.4 for required spectral interference test cri- teria.

    - When  interelement  corrections   are not used, either on-going SIC solutions (Sec- tion 7.14) must be analyzed to verify the ab- sence  of  interelement  spectral   interference or a computer software routine must be em- ployed for comparing the  determinative  data to limits files for notifying  the  analyst  when an interfering element is detected in the sample at a concentration that will produce either an  apparent false positive concentra- tion, greater than the analyte IDL, or false negative  analyte   concentration,   less   than the 99% lower control limit of the calibra- tion  blank.  When  the  interference   accounts for 10% or more of the analyte concentra- tion, either an alternate wavelength free of interference or another approved test proce- dure must be used to complete  the  analysis. For example, the copper peak at 213.853 nm could be mistaken for the zinc peak at 213.856 nm  in  solutions  with  high  copper  and  low zinc concentrations. For this example,  a spectral scan in the 213.8 nm region  would not reveal the misidentification because a single peak near the zinc location would be observed. The possibility of this misidentification of copper  for  the  zinc  peak at 213.856 nm can be identified by measuring the copper at another emission line, e.g., 324.754 nm. Users should be aware that, de- pending upon the instrumental resolution, alternate wavelengths with adequate sensi- tivity  and  freedom  from  interference  may not be available for all matrices. In these circumstances the analyte must be deter- mined using another approved test  proce- dure.

  - Physical interferences are effects asso- ciated with the sample nebulization and transport processes. Changes in viscosity and surface tension can cause significant inac- curacies,  especially  in  samples  containing

#### Pt. 136, App. C

high dissolved solids or high acid concentra- tions. If physical interferences are present, they must be reduced by such means as a high-solids nebulizer, diluting the sample, using a peristaltic pump, or using an appro- priate internal standard element. Another problem that can occur with high dissolved solids is salt buildup at the tip of the nebulizer, which affects aerosol flow rate and causes instrumental drift. This problem can be controlled by a high-solids nebulizer, wet- ting the argon prior to nebulization, using a tip washer, or diluting the sample. Also, it has been reported that better control of the argon flow rates, especially for the nebulizer, improves instrument stability and precision; this is accomplished with the use of mass flow controllers.

  - Chemical interferences include molec- ular-compound formation, ionization effects, and solute-vaporization effects. Normally, these effects are not significant with the ICP–AES technique. If observed, they can be minimized by careful selection of operating conditions (such as incident power and obser- vation height), by buffering of the sample, by matrix matching, and by standard-addition procedures. Chemical interferences are high- ly dependent on matrix type and the specific analyte element.

  - Memory interferences result when analytes in a previous sample contribute  to the signals measured in a new sample. Mem- ory effects can result from sample deposition on the uptake tubing to the nebulizer, and from the buildup of sample material in the plasma torch and spray chamber. The site where these effects occur is dependent on the element and can be minimized by  flushing the system with a rinse blank between sam- ples (Section 7.10.4). The possibility of mem- ory interferences should be recognized with- in an analytical run and suitable rinse times should be used to reduce them. The rinse times necessary for a particular  element must be estimated prior to analysis. This may be achieved by aspirating a standard containing elements corresponding to either their LDR or a concentration  ten  times those usually encountered. The aspiration time should be the same as a normal sample analysis period, followed by analysis of the rinse blank at designated intervals. The length of time required to reduce analyte signals to within a factor of two of the meth- od detection limit, should be noted. Until the required rinse time is established, this meth- od requires a rinse period of at least 60 sec- onds between samples and standards. If a memory interference is suspected, the sam- ple must be re-analyzed after a long rinse pe- riod.

5.0   Safety

  - The toxicity or carcinogenicity of each reagent used in this method have not

#### 40 CFR Ch. I (7–1–17 Edition)

been fully established. Each chemical should be regarded as a potential health hazard and exposure to these compounds should be as low as reasonably achievable. Each labora- tory is responsible for maintaining a current awareness file of OSHA regulations regard- ing the safe handling of the chemicals speci- fied in this method.9–12 A reference file of material data handling sheets should also be made available to all personnel involved in the chemical analysis. Specifically, con- centrated nitric and hydrochloric acids present various hazards and are moderately toxic and extremely irritating to skin and mucus membranes. Use these reagents in a fume hood whenever possible and if eye or skin contact occurs, flush with large vol- umes of water. Always wear safety glasses or a shield for eye protection, protective cloth- ing and observe proper mixing when working with these reagents.

  - The acidification of samples con- taining reactive materials may result in the release of  toxic gases, such as cyanides or sulfides. Acidification of samples should be done in a fume hood.

  - All personnel handling environmental samples known to contain or to have been in contact with human waste should be immu- nized against known disease causative agents.

  - The inductively coupled plasma should only be viewed with proper eye protection from the ultraviolet emissions.

  - It is the responsibility of the user  of this method  to  comply with  relevant  dis- posal and waste regulations. For guidance see Sections 14.0 and 15.0.

6.0   Equipment and Supplies

  - Inductively coupled plasma emission spectrometer:

    - Computer-controlled emission spec- trometer with background-correction capa- bility.

The spectrometer must be capable of  meet- ing and complying with the requirements de- scribed and referenced in Section 2.2.

    - Radio-frequency generator compliant with FCC regulations.

    - Argon gas supply—High purity grade (99.99%). When analyses are conducted fre- quently, liquid argon is more economical and requires less frequent replacement of tanks than compressed argon in conventional cyl- inders.

    - A variable speed peristaltic pump is required to deliver both standard and sample solutions to the nebulizer.

    - (Optional) Mass flow controllers to regulate the argon flow rates, especially the aerosol transport gas, are highly rec- ommended. Their use will provide more ex- acting control of reproducible plasma condi- tions.

#### Environmental Protection Agency	Pt. 136, App. C

  - Analytical balance, with capability to measure to 0.1 mg, for use in weighing solids, for preparing standards, and for determining dissolved solids in digests or extracts.

  - A temperature adjustable hot plate ca- pable of maintaining a temperature of 95 C.

  - (Optional) A temperature adjustable block digester capable of maintaining a tem- perature of 95 C and equipped with 250 mL constricted  digestion  tubes.

  - (Optional) A steel cabinet centrifuge with guard bowl, electric timer and brake.

  - A gravity convection drying oven with thermostatic control capable of maintaining 180 C 5 C.

  - (Optional)   An   air   displacement pipetter capable of delivering volumes rang- ing from 0.1–2500 L with an assortment of high  quality  disposable  pipet  tips.

  - Mortar and pestle, ceramic or non- metallic  material.

  - Polypropylene sieve, 5-mesh (4 mm opening).

  - Labware—For determination of trace levels of elements, contamination and loss are of prime consideration. Potential con- tamination sources include  improperly cleaned laboratory apparatus and general contamination within the laboratory envi- ronment from dust, etc. A clean laboratory work area designated for trace element sam- ple handling must be used. Sample con- tainers can introduce positive and negative errors in the determination of trace  ele- ments  by  contributing  contaminants through surface desorption or leaching, or depleting element concentrations through adsorption processes. All reusable labware (glass,  quartz,  polyethylene,  PTFE,   FEP, etc.) should be sufficiently clean for the task objectives. Several  procedures  found  to  pro- vide clean labware include washing with a detergent solution, rinsing with tap water, soaking for four hours or more in 20% (v/v) nitric acid or a mixture of HNO3  and HCl (1

+ 2 + 9), rinsing with reagent water and stor- ing clean. 2 3 Chromic acid cleaning solutions must be avoided because chromium is an analyte.

    - Glassware—Volumetric flasks, grad- uated cylinders, funnels and centrifuge tubes (glass and/or metal-free plastic).

    - Assorted calibrated pipettes.

    - Conical Phillips beakers (Corning 1080–250 or equivalent), 250 mL with 50 mm watch glasses.

    - Griffin beakers, 250 mL with 75 mm watch glasses and (optional) 75 mm ribbed watch   glasses.

    - (Optional) PTFE and/or quartz Grif- fin beakers, 250 mL with PTFE covers.

    - Evaporating dishes or high-form crucibles, porcelain, 100 mL capacity.

    - Narrow-mouth storage bottles, FEP (fluorinated ethylene propylene) with screw closure, 125 mL to 1 L capacities.

    - One-piece stem FEP wash bottle with screw closure, 125 mL capacity.

7.0   Reagents and Standards

  - Reagents may contain elemental im- purities which might affect analytical data. Only high-purity reagents that conform to the American Chemical Society specifica- tions 13 should be used whenever possible. If the purity of a reagent is in question, ana- lyze for contamination. All acids used for this method must be of ultra high-purity grade or equivalent. Suitable acids are avail- able from a number of manufacturers. Redis- tilled acids prepared by sub-boiling distilla- tion are acceptable.

  - Hydrochloric acid, concentrated (sp.gr. 1.19)—HCl.

    - Hydrochloric acid (1 + 1)—Add 500 mL concentrated HCl to 400  mL  reagent water and dilute to 1 L.

    - Hydrochloric acid (1 + 4)—Add 200 mL concentrated HCl to 400  mL  reagent water and dilute to 1 L.

    - Hydrochloric acid (1 + 20)—Add 10 mL concentrated HCl to 200 mL  reagent water.

  - Nitric acid, concentrated (sp.gr. 1.41)— HNO3.

    - Nitric acid (1 + 1)—Add 500 mL con- centrated HNO3 to 400 mL reagent water and dilute to 1 L.

    - Nitric acid (1 + 2)—Add 100 mL con- centrated HNO3 to 200 mL reagent water.

    - Nitric acid (1 + 5)—Add 50 mL con- centrated HNO3 to 250 mL reagent water.

    - Nitric acid (1 + 9)—Add 10 mL con- centrated HNO3 to 90 mL reagent water.

  - Reagent water. All references to water in this method refer to ASTM Type I grade water.14

  - Ammonium hydroxide, concentrated (sp.gr. 0.902).

  - Tartaric acid, ACS reagent grade.

  - Hydrogen peroxide, 50%, stabilized cer- tified reagent grade.

  - Standard Stock Solutions—Stock standards may be purchased or prepared from ultra-high purity grade chemicals (99.99–99.999% pure). All compounds must be dried for one hour at 105 C, unless otherwise specified. It is recommended that stock solu- tions be stored in FEP bottles. Replace stock standards when succeeding dilutions for preparation of calibration standards cannot be verified.

CAUTION: Many of these chemicals are ex- tremely toxic if inhaled or swallowed (Sec- tion 5.1). Wash hands thoroughly after han- dling.

Typical stock solution preparation proce- dures follow for 1 L quantities, but for the purpose of pollution  prevention,  the  analyst is encouraged to prepare smaller quantities when possible. Concentrations are calculated based upon the weight of the pure element or upon the weight of the compound multiplied

#### Pt. 136, App. C

by  the  fraction  of  the  analyte  in  the  com- pound

#### 40 CFR Ch. I (7–1–17 Edition)

From pure element,

where: gravimetric factor = the weight frac- tion of the analyte in the compound

    - Aluminum solution, stock, 1 mL  = 1000 g Al: Dissolve 1.000 g of aluminum metal, weighed accurately to at least four significant figures, in an acid mixture  of  4.0 mL of (1 + 1) HCl and 1 mL of concentrated HNO3 in a beaker. Warm beaker slowly to ef- fect solution. When dissolution is complete, transfer solution quantitatively to  a  1  L flask, add an additional 10.0 mL of (1 + 1) HCl and dilute to volume with reagent water.

    - Antimony solution, stock, 1  mL  = 1000 g Sb: Dissolve 1.000 g of antimony pow- der, weighed accurately to at least four sig- nificant  figures,  in  20.0  mL  (1  +  1)  HNO3  and

10.0 mL concentrated HCl. Add 100 mL rea- gent water and 1.50 g tartaric acid. Warm so- lution  slightly  to  effect   complete   dissolu- tion. Cool solution and add reagent water to volume  in  a  1  L  volumetric  flask.

    - Arsenic  solution,  stock,  1  mL  =  1000

g  As:  Dissolve  1.320  g  of  As2O3   (As  fraction

= 0.7574), weighed accurately to at least four significant figures, in 100 mL of  reagent water containing 10.0  mL  concentrated NH4OH. Warm the solution gently to effect dissolution.  Acidify  the  solution  with  20.0 mL concentrated HNO3  and  dilute  to  volume in  a  1  L  volumetric  flask  with  reagent  water.

    - Barium  solution,  stock,  1  mL  =  1000

g Ba: Dissolve 1.437 g BaCO3 (Ba fraction = 0.6960), weighed accurately to at least four significant figures, in 150 mL (1 + 2) HNO3 with heating and stirring to degas and dis- solve compound. Let solution cool and dilute with  reagent  water  in  1  L  volumetric  flask.

    - Beryllium solution, stock, 1 mL  = 1000 g Be: DO NOT DRY. Dissolve 19.66 g BeSO44H2O (Be fraction = 0.0509), weighed accurately to at  least  four  significant  fig- ures, in reagent water, add 10.0 mL con- centrated HNO3,  and  dilute  to  volume  in  a  1 L  volumetric  flask  with  reagent  water.

    - Boron solution, stock, 1 mL = 1000 g B: DO NOT DRY. Dissolve 5.716 g anhydrous H3BO3 (B fraction = 0.1749), weighed accu- rately  to  at  least  four  significant  figures,  in

reagent water and dilute in a 1 L volumetric flask with reagent water. Transfer imme- diately after mixing to a clean FEP bottle to minimize any leaching of boron from the glass volumetric container. Use of a nonglass volumetric flask is recommended to avoid boron contamination from glassware.

    - Cadmium solution, stock, 1 mL  = 1000 g Cd: Dissolve 1.000 g Cd metal, acid cleaned with (1 + 9) HNO3, weighed accu- rately to at least four  significant  figures,  in 50 mL (1 + 1) HNO3 with heating to effect dis- solution. Let solution cool and dilute with reagent water in a 1 L volumetric flask.

    - Calcium  solution,  stock,  1  mL  =  1000

g Ca: Suspend 2.498 g CaCO3 (Ca fraction = 0.4005), dried at 180 C for one hour before weighing, weighed accurately to at least four significant figures, in reagent water and dis- solve cautiously with a  minimum  amount  of (1 + 1) HNO3. Add 10.0 mL concentrated HNO3 and  dilute  to  volume  in  a  1  L  volumetric flask  with  reagent  water.

    - Cerium  solution,  stock,  1  mL  =  1000

g Ce: Slurry 1.228 g CeO2 (Ce fraction  = 0.8141), weighed accurately to at least four significant figures, in 100 mL concentrated HNO3 and evaporate to dryness. Slurry the residue in 20 mL H2O, add 50 mL con- centrated HNO3, with heat and  stirring  add 60 mL 50% H2O2 dropwise in 1 mL increments allowing  periods  of  stirring  between  the   1 mL additions. Boil off excess H2O2 before di- luting to volume in a 1 L volumetric flask with  reagent  water.

    - Chromium   solution,   stock,   1   mL   = 1000 g Cr: Dissolve 1.923 g CrO3  (Cr fraction

= 0.5200), weighed accurately to at least four significant figures, in 120 mL (1 + 5) HNO3. When solution is complete,  dilute  to  volume in  a  1  L  volumetric  flask  with  reagent  water.

    - Cobalt  solution,  stock,  1  mL  =  1000

g Co: Dissolve 1.000 g Co metal, acid cleaned with (1 + 9) HNO3, weighed accurately to at least four significant figures, in 50.0 mL (1 +

- HNO3. Let solution cool and dilute to vol- ume in a 1 L volumetric flask with reagent water.

#### Environmental Protection Agency	Pt. 136, App. C

    - Copper  solution,  stock,  1  mL  =  1000

g Cu: Dissolve 1.000 g Cu metal, acid cleaned with (1 + 9) HNO3, weighed accurately to at least four significant figures, in 50.0 mL (1 +

  - HNO3 with heating to effect dissolution. Let solution cool and dilute in a 1 L volu- metric flask with reagent water.

    - Iron solution, stock, 1 mL = 1000 g Fe: Dissolve 1.000 g Fe metal, acid cleaned with (1 + 1) HCl, weighed accurately to four significant figures, in 100 mL (1 + 1) HCl with heating to effect  dissolution.  Let  solution cool and dilute with reagent water in a 1 L volumetric   flask.

    - Lead solution, stock, 1 mL = 1000 g Pb:  Dissolve  1.599  g  Pb(NO3)2   (Pb  fraction  =

0.6256), weighed accurately to at least four significant figures, in a  minimum  amount  of (1 + 1) HNO3. Add 20.0 mL (1 + 1) HNO3 and di-

lute to volume in a 1 L volumetric flask with reagent water.

    - Lithium solution,  stock,  1  mL  = 1000

g Li: Dissolve 5.324 g Li2CO3 (Li fraction = 0.1878), weighed accurately to at least four significant figures, in a  minimum  amount  of (1 + 1) HCl and dilute to volume in a 1 L vol- umetric  flask  with  reagent  water.

    - Magnesium solution, stock, 1 mL = 1000 g Mg: Dissolve 1.000 g cleanly polished Mg ribbon,  accurately  weighed  to  at  least four significant figures, in slowly added  5.0 mL (1 + 1) HCl (CAUTION: reaction is vig- orous). Add 20.0 mL  (1 + 1)  HNO3 and  dilute to volume in a 1 L volumetric flask  with  rea- gent  water.

    - Manganese solution, stock, 1 mL = 1000 g Mn: Dissolve 1.000 g of manganese metal, weighed accurately to at least four significant figures, in 50 mL (1 + 1) HNO3 and dilute to volume in a 1 L volumetric flask with  reagent  water.

    - Mercury solution, stock, 1 mL = 1000

g Hg: DO NOT DRY. CAUTION: highly toxic element. Dissolve 1.354 g HgCl2 (Hg fraction = 0.7388) in reagent water. Add 50.0 mL con- centrated HNO3 and dilute to volume in 1 L volumetric  flask  with  reagent  water.

    - Molybdenum  solution,  stock,  1  mL

= 1000 g Mo: Dissolve 1.500 g MoO3 (Mo frac- tion = 0.6666), weighed accurately to at least four significant figures, in a mixture  of  100 mL reagent water and 10.0 mL concentrated NH4OH, heating to effect dissolution. Let so- lution cool and dilute with reagent water in a 1 L volumetric flask.

    - Nickel  solution,  stock,  1  mL  =  1000

g Ni: Dissolve 1.000 g of nickel metal, weighed accurately  to  at  least  four  signifi- cant figures, in 20.0 mL  hot  concentrated HNO3, cool, and dilute to volume in a 1 L vol- umetric  flask  with  reagent  water.

    - Phosphorus solution, stock, 1 mL = 1000 g P: Dissolve 3.745 g NH4H2PO4 (P frac- tion = 0.2696), weighed accurately to at least four significant figures, in 200  mL  reagent water and dilute to volume in a 1 L volu- metric  flask  with  reagent  water.

    - Potassium solution, stock, 1 mL  = 1000 g K: Dissolve 1.907 g KCl (K fraction = 0.5244) dried at 110 C, weighed accurately to at least four significant figures, in  reagent water, add 20 mL (1 + 1) HCl and dilute to volume in a 1 L volumetric flask with rea- gent  water.

    - Selenium solution, stock, 1  mL  = 1000 g Se: Dissolve 1.405 g SeO2  (Se fraction

= 0.7116), weighed  accurately to  at least  four significant figures, in 200 mL reagent water and  dilute  to  volume  in  a  1  L  volumetric flask  with  reagent  water.

    - Silica  solution,  stock,  1  mL  =  1000

g SiO2: DO NOT DRY. Dissolve 2.964 g (NH4)2SiF6, weighed accurately  to  at  least four significant figures, in 200 mL (1  +  20) HCl with heating at 85 C to effect dissolu- tion. Let solution cool  and  dilute  to  volume in a 1 L volumetric flask with reagent water.

    - Silver  solution,  stock,  1  mL  =  1000

g Ag: Dissolve 1.000 g Ag metal, weighed ac- curately to at least four significant figures, in 80 mL (1 + 1) HNO3 with heating to effect dissolution. Let solution cool and dilute with reagent water in a 1 L volumetric flask. Store solution in amber bottle or wrap bottle completely with aluminum foil to protect so- lution from light.

    - Sodium  solution,  stock,  1  mL  =  1000

g Na: Dissolve 2.542 g NaCl (Na fraction = 0.3934), weighed accurately to at least four significant figures, in reagent water. Add  10.0 mL concentrated HNO3  and  dilute  to  volume in  a  1  L  volumetric  flask  with  reagent  water.

    - Strontium solution, stock, 1  mL  = 1000 g Sr: Dissolve 1.685 g SrCO3  (Sr fraction

= 0.5935), weighed accurately to at least four significant figures, in 200 mL reagent water with dropwise addition of 100 mL (1 + 1) HCl. Dilute to volume in a 1 L volumetric flask with  reagent  water.

    - Thallium solution, stock, 1 mL  = 1000 g Tl: Dissolve 1.303 g TlNO3  (Tl fraction

= 0.7672), weighed  accurately to  at least  four significant figures, in reagent water. Add  10.0 mL concentrated HNO3  and  dilute  to  volume in  a  1  L  volumetric  flask  with  reagent  water.

    - Tin  solution,  stock,  1  mL  =  1000  g

Sn: Dissolve 1.000 g Sn shot, weighed accu- rately to at least four  significant  figures,  in an acid mixture of 10.0 mL concentrated HCl and 2.0 mL (1 + 1) HNO3 with heating to ef- fect dissolution. Let solution cool, add  200 mL concentrated HCl, and  dilute  to  volume in a 1 L volumetric flask with reagent water.

    - Titanium solution, stock, 1 mL  = 1000 g Ti: DO NOT DRY. Dissolve 6.138 g (NH4)2TiO(C2O4)2H2O (Ti fraction = 0.1629), weighed accurately to at least four signifi- cant figures, in 100 mL reagent water. Dilute to volume in a 1 L volumetric flask with rea- gent water.

    - Vanadium solution, stock, 1 mL  = 1000 g V: Dissolve 1.000 g V metal, acid cleaned with (1 + 9)  HNO3,  weighed  accu- rately  to  at  least  four  significant  figures,  in

#### Pt. 136, App. C

50 mL (1 + 1) HNO3 with heating to effect dis- solution. Let solution cool and dilute with reagent water to volume in a 1 L volumetric flask.

    - Yttrium  solution,  stock  1  mL  =  1000

g Y: Dissolve 1.270 g Y2O3 (Y fraction  = 0.7875), weighed accurately to at least four significant figures, in 50 mL (1 + 1) HNO3, heating to effect dissolution.  Cool  and  dilute to volume in a 1 L volumetric flask  with  rea- gent  water.

    - Zinc solution, stock, 1 mL = 1000 g Zn: Dissolve 1.000 g Zn metal, acid cleaned with (1 + 9) HNO3, weighed accurately to at least four significant figures, in 50 mL (1 + 1) HNO3 with heating to effect dissolution. Let solution cool and dilute  with  reagent  water to volume in a 1 L volumetric flask.

  - Mixed Calibration Standard Solu- tions—For the analysis of total recoverable digested samples prepare mixed calibration standard solutions (see Table 3) by com- bining appropriate volumes of the stock so- lutions in 500 mL volumetric flasks con- taining 20 mL (1 + 1) HNO3 and 20 mL (1 + 1) HCl and dilute to volume with  reagent water. Prior to preparing the mixed stand- ards, each stock solution should be analyzed separately to determine possible spectral interferences or the presence of impurities. Care should be taken when preparing the mixed standards to ensure that the elements are compatible and stable together. To mini- mize the opportunity for contamination by the containers, it is recommended to  trans- fer the mixed-standard solutions to acid- cleaned, never-used FEP fluorocarbon (FEP) bottles for storage. Fresh mixed standards should be prepared, as needed, with the real- ization that concentrations can change on aging. Calibration standards not prepared from primary standards must be initially verified using a certified reference solution. For the recommended wavelengths listed in Table 1 some typical calibration standard combinations are given in Table 3.

Note: If the addition of silver to the rec- ommended mixed-acid calibration standard results in an initial precipitation, add 15 mL of reagent water and warm the  flask  until the solution clears. For this acid combina- tion, the silver concentration should be lim- ited to 0.5 mg/L.

  - Blanks—Four types of blanks are re- quired for the analysis. The calibration blank is used in establishing the analytical curve, the laboratory reagent blank is used to assess possible contamination from the sample preparation procedure, the labora- tory fortified blank is used to assess routine laboratory performance and a rinse blank is used to flush the instrument uptake system and nebulizer between standards, check solu- tions, and samples to reduce memory inter- ferences.

#### 40 CFR Ch. I (7–1–17 Edition)

    - The calibration blank for aqueous samples and extracts is prepared by acidifying reagent water to the same con- centrations of the acids as used for the standards. The calibration blank should be stored in a FEP bottle.

    - The laboratory reagent blank (LRB) must contain all the reagents in the same volumes as used in the processing of the samples. The LRB must be carried through the same entire preparation scheme as the samples including sample digestion, when applicable.

    - The  laboratory   fortified   blank (LFB) is prepared by fortifying an aliquot of the laboratory reagent blank with all analytes to  a  suitable concentration  using the following recommended criteria: Ag 0.1 mg/L, K 5.0 mg/L and all other analytes 0.2 mg/L or a concentration approximately 100 times their respective MDL, whichever is greater. The LFB must be carried  through the same entire preparation scheme as the samples including sample digestion, when applicable.

    - The rinse blank is prepared by acidifying reagent water to the same con- centrations of acids as used in the calibra- tion blank and stored in a convenient man- ner.

  - Instrument Performance Check (IPC) Solution—The IPC solution is used to peri- odically verify instrument performance dur- ing analysis. It should be prepared in the same acid mixture as the calibration stand- ards by combining method analytes at appro- priate concentrations. Silver  must  be  lim- ited to <0.5 mg/L; while potassium and phos- phorus because of higher MDLs and silica be- cause of potential contamination  should  be at concentrations of 10 mg/L. For other analytes a concentration of 2 mg/L is rec- ommended. The IPC solution should be pre- pared from the same standard stock solu- tions used to prepare the calibration stand- ards and stored in an FEP bottle. Agency programs may specify or request that addi- tional instrument performance check solu- tions be prepared at specified concentrations in order to meet particular program needs.

  - Quality Control Sample (QCS)—Anal- ysis of a QCS is required for initial  and  peri- odic verification of calibration standards  or stock standard solutions in order to verify instrument performance. The QCS must be obtained from an outside source  different from the standard stock solutions and pre- pared in the same acid mixture as the cali- bration standards. The concentration of the analytes in the QCS solution should be 1 mg/ L, except silver, which must be limited to a concentration of 0.5 mg/L for  solution  sta- bility. The  QCS  solution  should  be  stored  in a FEP bottle and analyzed as needed to meet data-quality  needs.  A  fresh   solution   should be prepared quarterly or more frequently as needed.

#### Environmental Protection Agency	Pt. 136, App. C

  - Spectral Interference Check (SIC) So- lutions—When interelement corrections are applied, SIC solutions are needed containing concentrations of the interfering elements at levels that will provide an adequate test of the correction factors.

    - SIC solutions containing (a) 300 mg/ L Fe; (b) 200 mg/L AL; (c) 50 mg/L Ba; (d) 50 mg/L Be; (e) 50 mg/L Cd; (f) 50 mg/L Ce; (g) 50 mg/L Co; (h) 50 mg/L Cr; (i) 50 mg/L Cu; (j) 50 mg/L Mn; (k) 50 mg/L Mo; (l) 50 mg/L Ni; (m) 50 mg/L Sn; (n) 50 mg/L SiO2; (o) 50 mg/L Ti;

(p) 50 mg/L Tl and (q) 50 mg/L V should be prepared in the same acid mixture as the calibration standards and stored in FEP bot- tles. These solutions can be used to periodi- cally verify a partial list of the on-line (and possible off-line) interelement spectral cor- rection factors for the recommended wave- lengths given in Table 1.  Other  solutions could achieve the same objective as well. (Multielement SIC solutions3 may be pre- pared and substituted for the single element solutions provided an analyte  is  not  subject to interference from more than one interferant in the solution.)

Note: If wavelengths other than those rec- ommended in Table 1 are used, other solu- tions  different  from  those  above  (a  through

q) may be required.

    - For interferences from iron and alu- minum, only those correction factors (posi- tive or negative) when multiplied by 100 to calculate apparent  analyte  concentrations that exceed the determined analyte IDL  or fall below the lower 3-sigma control limit of the calibration blank need be tested on a daily  basis.

    - For the other interfering elements, only those correction factors (positive or negative) when multiplied by 10 to calculate apparent analyte concentrations that exceed the determined analyte IDL or fall below the lower 3-sigma control limit of the calibra- tion blank need be tested on a daily basis.

    - If the correction routine is oper- ating properly, the determined apparent analyte(s) concentration from analysis of each interference solution (a through q) should fall within a specific concentration range bracketing the calibration blank. This concentration range is calculated by multi- plying the concentration of the interfering element by the value of the correction factor being tested and dividing by 10. If after sub- traction of the calibration blank the appar- ent analyte concentration is outside (above or below) this range, a change in the correc- tion factor of more than 10% should be sus- pected. The cause of the change should be de- termined and corrected and the correction factor should be updated.

Note: The SIC solution should be analyzed more than once to confirm a change has oc- curred with adequate rinse time between so-

lutions and before subsequent analysis of the calibration blank.

    - If the correction factors tested on a daily basis are found to be within the 10% criteria for five consecutive days, the re- quired verification frequency of  those  factors in compliance may be extended to a weekly basis. Also, if the nature of the samples ana- lyzed is such (e.g., finished drinking water) that  they  do  not  contain  concentrations   of the interfering elements at the 10 mg/L level, daily  verification  is  not  required;   however, all interelement spectral correction factors must be verified annually and updated, if necessary.

    - If the instrument does not display negative concentration  values,  fortify  the SIC solutions with the  elements  of  interest at 1 mg/L and test for analyte recoveries that are below 95%. In the absence of meas- urable analyte, over-correction could go un- detected because a negative value could be reported as zero.

  - For instruments without interele- ment correction capability or when interele- ment corrections are not used, SIC solutions (containing similar concentrations of the major components in the samples, e.g., 10 mg/L) can serve to verify the absence of ef- fects at the wavelengths selected. These data must be kept on file with the sample  anal- ysis data. If the SIC solution confirms an op- erative interference that is 10% of the analyte concentration, the analyte must be determined using a wavelength and back- ground correction  location  free of  the  inter- ference or by another approved test proce- dure. Users are advised that high salt con- centrations can cause analyte signal sup- pressions and confuse interference tests.

  - Plasma Solution—The  plasma  solu- tion is used for determining the optimum viewing height of the plasma above the  work coil prior to using the method (Section  10.2). The solution is prepared by adding a 5 mL al- iquot from each of the stock standard solu- tions of arsenic, lead,  selenium,  and  thallium to a mixture of 20 mL (1 + 1) nitric acid and 20 mL (1 +  1)  hydrochloric  acid  and  diluting to  500  mL  with  reagent  water.  Store  in   a FEP    bottle.

8.0  Sample Collection, Preservation, and Storage

  - Prior to the collection of an aqueous sample, consideration should be given to the type of data required, (i.e., dissolved or total recoverable), so that appropriate preserva- tion and pretreatment steps can be taken. The pH of all aqueous samples must be test- ed immediately prior to aliquoting for proc- essing or ‘‘direct analysis’’ to ensure the sample has been properly preserved. If prop- erly acid preserved, the sample  can  be  held up to six months before analysis.

#### Pt. 136, App. C

  - For the determination of the dissolved elements, the sample must be filtered through a 0.45 m pore diameter membrane filter at the time of collection or as soon thereafter as practically possible. (Glass or plastic filtering apparatus are recommended to avoid possible contamination. Only plas- tic apparatus should be used when the deter- minations of boron and silica are critical.) Use a portion of the filtered sample to rinse the filter flask, discard this portion and col- lect the required volume of filtrate. Acidify the filtrate with (1 + 1) nitric acid imme- diately following filtration to pH <2.

  - For the determination of total recov- erable elements in aqueous samples, samples are not filtered, but acidified with (1 + 1) ni- tric acid to pH <2 (normally, 3 mL of (1 + 1) acid per liter of sample is sufficient for most ambient and drinking water samples). Pres- ervation may be done at the time of collec- tion, however, to avoid the hazards of strong acids in the  field, transport  restrictions, and possible contamination it is recommended that the samples be returned to the labora- tory within two weeks of collection and acid preserved upon receipt in the laboratory. Following  acidification,  the  sample  should be mixed, held for 16 hours, and then verified to be pH <2 just prior withdrawing an aliquot for processing or ‘‘direct  analysis’’.  If  for some reason such as high alkalinity the sam- ple pH is verified to be >2, more acid must be added and the sample held for 16 hours until verified to be pH <2. See Section 8.1.

Note: When the nature of the sample is ei- ther unknown or is known to be hazardous, acidification should be done in a fume hood. See Section 5.2.

  - Solid samples require no preservation prior to analysis other than storage at 4 C. There is no established holding time limita- tion for solid samples.

  - For aqueous samples, a field blank should be prepared and analyzed as required by the data user. Use the same container and acid as used in sample collection.

9.0   Quality Control

  - Each laboratory using this method is required to operate a formal quality control (QC) program. The minimum requirements of this program consist of an initial demonstra- tion of laboratory capability, and the peri- odic analysis of laboratory reagent blanks, fortified blanks and other laboratory solu- tions as a continuing check on performance. The laboratory is required to maintain per- formance records that define the quality  of the data thus generated.

  - Initial Demonstration of Performance (mandatory).

    - The initial demonstration of per- formance is used to characterize instrument performance (determination of linear dy- namic ranges and analysis of quality control

#### 40 CFR Ch. I (7–1–17 Edition)

samples) and laboratory performance (deter- mination of method detection  limits)  prior to analyses conducted by this method.

    - Linear dynamic range (LDR)—The upper limit of the LDR must be established for each wavelength utilized. It must be de- termined from a linear calibration prepared in the normal manner using the established analytical operating procedure for the in- strument. The LDR should be determined by analyzing succeedingly higher standard con- centrations of the analyte until the observed analyte concentration is no more than 10% below the stated concentration of the stand- ard. Determined LDRs must be documented and kept on file. The LDR which may be used for the analysis of samples should be judged by the analyst from the resulting data. Determined sample analyte concentra- tions that are greater than 90% of the deter- mined upper LDR limit must be diluted and reanalyzed. The LDRs should be verified an- nually or whenever, in the judgment of the analyst, a change in analytical performance caused by either a change in instrument hardware or operating conditions would dic- tate they be redetermined.

    - Quality control sample (QCS)—When beginning the use of this method, on a quar- terly basis, after the preparation of stock or calibration standard solutions or as required to meet data-quality needs, verify the cali- bration standards and acceptable instrument performance with the preparation and anal- yses of a QCS (Section 7.12). To verify the calibration standards the determined mean concentrations from three analyses of the QCS must be within 5% of the stated values. If the calibration standard cannot be verified, performance of the determinative step of the method is unacceptable. The source of the problem must be identified and corrected before either proceeding on with the initial determination of method detec- tion limits or continuing with on-going anal- yses.

    - Method detection limit (MDL)— MDLs must be established for all wave- lengths utilized, using reagent water (blank) fortified at a concentration of two to three times the estimated instrument detection limit.15 To determine MDL values, take seven replicate aliquots of the fortified rea- gent water and process through the entire analytical method. Perform all calculations defined in the method and report the con- centration values in the appropriate units. Calculate the MDL as follows:

MDL = (t) (S)

where:

t = students’ t value for a 99% confidence level and a standard deviation estimate with n-1 degrees of freedom [t = 3.14 for seven replicates]

S = standard deviation of the replicate anal- yses

#### Environmental Protection Agency	Pt. 136, App. C

Note: If additional confirmation is desired, reanalyze the seven replicate aliquots on two more nonconsecutive days and again cal- culate the MDL values for each day. An aver- age of the three MDL values for each analyte may provide for a more appropriate MDL es- timate. If the relative standard deviation (RSD) from the analyses of the seven aliquots is <10%, the concentration used to determine the analyte MDL may have been inappropriately high for the determination. If so, this could result in the calculation of an unrealistically low MDL. Concurrently, determination of MDL in reagent water rep- resents a best case situation and does not re- flect possible matrix effects of real world samples. However, successful analyses of LFMs (Section 9.4) and the analyte addition test described in Section 9.5.1 can give con- fidence to the MDL value determined in rea- gent water. Typical single laboratory MDL values using this method are given in Table 4.

The MDLs must be sufficient to detect analytes at the required levels according to compliance monitoring regulation (Section 1.2). MDLs should be determined annually, when a new operator begins work or when-

ever, in the judgment of the analyst,  a change in analytical performance caused by either a change in instrument hardware or operating conditions would dictate they be redetermined.

9.3 Assessing Laboratory Performance (mandatory)

9.3.1  Laboratory  reagent   blank   (LRB)— The laboratory  must  analyze  at  least  one LRB (Section 7.10.2) with each batch of 20 or fewer samples of the same matrix.  LRB  data are used to assess contamination from the laboratory environment. LRB values that ex- ceed the MDL indicate laboratory or reagent contamination  should  be  suspected.   When LRB values constitute 10% or more of the analyte  level  determined  for  a  sample  or  is

2.2 times the analyte MDL whichever is greater, fresh aliquots of the samples must be prepared and analyzed again for the af- fected analytes after the source of contami- nation has been corrected and acceptable LRB values have been obtained.

    - Laboratory fortified blank (LFB)— The laboratory must analyze at least one LFB (Section 7.10.3) with each batch of sam- ples. Calculate accuracy as percent recovery using the following equation:

where:

R = percent recovery

LFB = laboratory fortified blank LRB = laboratory reagent blank

s   =   concentration   equivalent   of   analyte added to fortify the LBR solution

If the recovery of any analyte falls outside the required control limits of 85–115%, that analyte is judged out of control,  and  the source of the problem should be identified and resolved before continuing analyses.

    - The laboratory must  use  LFB  anal- yses data to assess laboratory performance against the required control limits of  85– 115% (Section 9.3.2). When sufficient internal performance  data   become   available   (usually a minimum of 20–30 analyses), optional con- trol limits can be developed from the mean percent recovery (x) and the standard devi- ation  (S)  of  the  mean   percent   recovery. These data can be used to establish the upper and  lower  control  limits  as  follows:

UPPER CONTROL LIMIT = x + 3S LOWER CONTROL LIMIT = x ¥ 3S

The optional control limits  must  be  equal to or better than  the  required  control  limits of 85–115%. After each five to 10 new recovery measurements, new control limits can be calculated  using  only  the  most  recent  20–30

data points. Also, the standard deviation (S) data should be used to establish an on-going precision statement for the level of con- centrations included in the LFB. These data must be kept on file and be available for re- view.

    - Instrument performance check (IPC) solution—For all determinations the labora- tory must analyze the IPC solution (Section 7.11) and a calibration blank immediately following daily calibration, after every 10th sample (or more frequently, if required) and at the end of the sample run. Analysis of the calibration blank should always be <the analyte IDL,  but greater than the lower 3- sigma control limit of the calibration blank. Analysis of the IPC solution immediately following calibration must verify that the instrument is within 5% of calibration with a relative standard deviation <3% from rep- licate integrations 4. Subsequent analyses of the IPC solution must be within 10% of cali- bration. If the calibration cannot be verified within the specified limits, reanalyze either or both the IPC solution and the calibration

#### Pt. 136, App. C

blank. If the second analysis of the IPC solu- tion or the calibration blank confirm cali- bration to be outside the limits, sample anal- ysis must be discontinued, the cause deter- mined, corrected and/or the instrument re- calibrated. All samples following the last ac- ceptable IPC solution must be reanalyzed. The analysis data of the calibration blank and IPC solution must be kept on file with the sample analyses data.

    - Spectral interference check (SIC) so- lution—For all determinations the labora- tory must periodically verify the interele- ment spectral interference correction rou- tine by analyzing SIC solutions. The prepa- ration and required periodic analysis of SIC solutions and test criteria for verifying the interelement interference correction routine are given in Section 7.13. Special cases where on-going verification is required are de- scribed in Section 7.14.

  - Assessing Analyte Recovery and Data Quality.

    - Sample homogeneity and the chem- ical nature of the sample matrix can affect analyte recovery and the quality of the data. Taking separate aliquots from the sample for replicate and fortified analyses can in some cases assess the effect. Unless otherwise specified by the data user, laboratory or pro- gram, the following laboratory fortified ma- trix (LFM) procedure (Section 9.4.2) is re- quired. Also, other tests such as the analyte addition test (Section 9.5.1) and sample dilu- tion test (Section 9.5.2) can indicate if  ma- trix effects are operative.

    - The laboratory must add a known amount of each analyte to a minimum of 10% of the routine samples. In each case the LFM aliquot must be a duplicate of the ali- quot used for sample analysis and for total recoverable determinations added prior to sample preparation. For water samples, the

#### 40 CFR Ch. I (7–1–17 Edition)

added analyte concentration must be  the same as that used in the laboratory fortified blank (Section 7.10.3). For solid samples, however, the concentration added should be expressed as mg/kg and is calculated for  a one gram aliquot by multiplying the added analyte concentration (mg/L) in solution by the conversion factor 100 (mg/L 0.1L/0.001kg

= 100, Section 12.5). (For notes on Ag, Ba, and Sn see Sections 1.7 and 1.8.) Over time, sam- ples from all routine sample  sources  should be fortified.

Note: The concentration of calcium, mag- nesium, sodium and strontium in environ- mental waters, along with iron and alu- minum in solids can vary greatly and are not necessarily predictable. Fortifying these analytes in routine samples at the same con- centration used for the LFB may prove to be of little use in assessing data quality for these analytes. For these analytes sample di- lution and reanalysis using the criteria given in Section 9.5.2 is recommended. Also, if specified by the data user, laboratory or pro- gram, samples can be fortified at higher con- centrations, but even major constituents should be limited to <25 mg/L so as not to alter the sample matrix and affect the anal- ysis.

    - Calculate the percent recovery for each analyte, corrected for background con- centrations measured in the unfortified sam- ple, and compare these values to the des- ignated LFM recovery range of 70–130% or a 3-sigma recovery range calculated from the regression equations given in Table 9.16 Re- covery calculations are not required if the concentration added is less than 30% of the sample background concentration. Percent recovery may be calculated in units appro- priate to the matrix, using the following equation:

where:

R = percent recovery

Cs = fortified sample concentration

C = sample background concentration

s   =   concentration   equivalent   of   analyte added to fortify the sample

    - If the recovery of any analyte falls outside the designated LFM recovery range, and the laboratory performance for that analyte is shown to be in control (Section 9.3), the recovery problem encountered with the fortified sample is judged to be matrix related, not system related. The data user should be informed that the result for that analyte in the unfortified sample is suspect

due to either the heterogeneous nature  of the sample or matrix effects and analysis by method of standard addition or the use of an internal standard(s) (Section 11.5) should be considered.

    - Where reference materials are avail- able, they should be analyzed to provide ad- ditional performance data. The analysis of reference samples is a valuable tool for dem- onstrating the ability to perform the method acceptably. Reference materials containing high concentrations of analytes can provide additional information on the performance of the spectral interference correction rou- tine.

#### Environmental Protection Agency	Pt. 136, App. C

  - Assess the possible need for the meth- od of standard additions (MSA) or internal standard elements by the following tests. Di- rections for using MSA or internal stand- ard(s) are given in Section 11.5.

    - Analyte addition test: An analyte(s) standard added to a portion of a prepared sample, or its dilution,  should  be  recovered to within 85% to 115% of the known  value. The analyte(s) addition should produce a minimum level of 20  times  and  a  maximum of 100 times the method detection  limit.  If the analyte addition is <20% of the sample analyte  concentration,  the   following   dilu- tion test should be used. If recovery of the analyte(s) is  not  within  the  specified  limits, a matrix effect should be suspected, and the associated data flagged  accordingly.  The method of additions or the use of an appro- priate internal standard  element  may  pro- vide  more  accurate  data.

    - Dilution test: If the analyte con- centration is sufficiently high (minimally, a factor of 50 above the instrument detection limit in the original solution but <90% of the linear limit), an analysis of a 1 + 4 dilution should agree (after correction for the fivefold dilution) within 10% of the original deter- mination. If not, a chemical or physical in- terference effect should be suspected and the associated data flagged  accordingly.  The method of standard additions or  the  use  of an internal-standard  element  may  provide more accurate  data  for  samples  failing  this test.

10.0   Calibration and Standardization

  - Specific wavelengths are listed in Table 1. Other wavelengths may be sub- stituted if they can provide the needed sensi- tivity and are corrected for spectral inter- ference. However, because of the difference among various makes and models of spec- trometers, specific instrument operating conditions cannot be given. The instrument and operating conditions utilized for deter- mination must be capable  of  providing  data of acceptable  quality  to  the  program  and data user. The analyst should follow the in- structions provided by the instrument manu- facturer unless other conditions provide similar or better performance for a task. Op- erating conditions for aqueous solutions usu- ally vary from 1100–1200 watts forward power, 15–16 mm viewing height, 15–19 L/min. argon coolant flow, 0.6–1 L/min. argon aerosol flow, 1–1.8 mL/min. sample pumping rate with a one minute preflush time and measurement time near 1 s per wavelength peak (for se- quential instruments) and near 10 s per sam- ple (for simultaneous instruments). Use of the Cu/Mn intensity ratio at 324.754 nm and 257.610 nm (by adjusting the argon aerosol flow) has been recommended as a way to achieve repeatable interference correction factors.17

  - Prior to using this method optimize the plasma operating conditions. The fol- lowing procedure is recommended for vertically configured plasmas. The purpose of plasma optimization is to provide a max- imum signal-to-background ratio for the least sensitive element in the analytical array. The use of a mass flow controller to regulate the nebulizer gas flow rate greatly facilitates the procedure.

    - Ignite the  plasma  and  select  an  ap- propriate incident rf power with minimum reflected power. Allow the instrument to be- come  thermally  stable  before  beginning. This usually requires at least 30 to 60 min- utes of operation. While aspirating the 1000

g/mL solution of yttrium (Section 7.8.32), follow the instrument manufacturer’s in- structions and adjust the aerosol carrier gas flow rate through the nebulizer so a  defini- tive blue emission region of the plasma ex- tends approximately from 5–20 mm above the top of the work coil.18 Record  the  nebulizer gas flow rate or pressure setting for future reference.

    - After establishing the nebulizer gas flow rate, determine the solution uptake rate of the nebulizer in mL/min. by aspi- rating a known volume calibration blank for a period of at least three minutes. Divide the spent volume by the aspiration time (in min- utes) and record the uptake rate. Set the peristaltic pump to deliver the uptake rate in a steady even flow.

    - After horizontally aligning the plas- ma and/or optically profiling the spectrom- eter, use the selected instrument conditions from Sections 10.2.1 and 10.2.2, and aspirate the plasma solution (Section 7.15), con- taining 10 g/mL each of As, Pb, Se and Tl. Collect intensity data at  the  wavelength peak for each analyte at 1 mm intervals from 14–18 mm above the top of the work coil. (This region of the plasma is commonly re- ferred to as the analytical  zone.)19  Repeat the process using the calibration blank. De- termine the net  signal  to  blank  intensity ratio for each analyte for each  viewing height setting. Choose the height for viewing the plasma that provides the largest inten- sity ratio for the least sensitive  element  of the four analytes. If more than one position provides the same ratio, select the position that provides the  highest  net  intensity counts for the least sensitive element or ac- cept a compromise position of the intensity ratios of all four analytes.

    - The instrument operating condition finally selected as being optimum should provide the lowest reliable instrument detec- tion limits and method detection limits. Refer to Tables 1 and 4 for comparison of IDLs  and  MDLs,  respectively.

    - If either the instrument operating conditions, such as incident power and/or nebulizer gas flow rate are changed, or a new torch injector tube having a different orifice

#### Pt. 136, App. C

i.d. is installed, the plasma and plasma view- ing height should be reoptimized.

    - Before daily calibration and after the instrument warmup period, the nebulizer gas flow must be reset to the determined op- timized flow. If a mass flow controller is being used, it should be reset to the recorded optimized flow rate. In order to maintain valid spectral interelement correction rou- tines the nebulizer gas flow rate should be the same from day-to-day (<2% change). The change in signal intensity with a change in nebulizer gas flow rate for both ‘‘hard’’ (Pb

220.353 nm) and ‘‘soft’’ (Cu 324.754) lines is il- lustrated in Figure 1.

  - Before using the procedure (Section 11.0) to analyze samples, there must be data available documenting initial demonstration of performance. The required data and proce- dure is described in Section 9.2. This data must be generated using the same instru- ment operating conditions and calibration routine (Section 11.4) to be used for sample analysis. These documented data  must  be kept on file and be available  for  review  by the data user.

  - After completing the initial dem- onstration of performance, but before ana- lyzing samples, the laboratory must estab- lish and initially verify an interelement spectral  interference  correction  routine  to be used during sample analysis. A general de- scription  concerning  spectral  interference and the analytical requirements for back- ground correction and for correction of interelement spectral interference in par- ticular are given in Section 4.1. To determine the appropriate location for background cor- rection and to establish the interelement in- terference correction routine, repeated spec- tral scan about the analyte wavelength and repeated analyses of the single element solu- tions may be required. Criteria for deter- mining an interelement spectral interference is an apparent positive or negative con- centration on the analyte that is outside the 3-sigma control limits of the calibration blank for the analyte.  (The  upper-control limit is the analyte IDL.) Once  established, the entire routine must be initially and peri- odically verified annually, or whenever there is a change in instrument operating condi- tions (Section 10.2.5). Only a portion of the correction routine must be verified more fre- quently or on a daily basis. Test criteria and required  solutions  are  described  in  Section

7.13. Initial and periodic verification data of the routine should be kept on file. Special cases where on-going verification are re- quired is described in Section 7.14.

11.0   Procedure

11.1   Aqueous Sample Preparation— Dissolved  Analytes

11.1.1 For the determination of dissolved analytes in ground and surface waters, pipet

#### 40 CFR Ch. I (7–1–17 Edition)

an aliquot (20 mL) of the filtered, acid pre- served sample into a 50 mL polypropylene centrifuge tube. Add an  appropriate  volume of (1 + 1) nitric acid to adjust the acid con- centration  of  the  aliquot  to  approximate  a 1% (v/v) nitric acid solution (e.g., add 0.4 mL (1 + 1) HNO3 to a 20  mL  aliquot  of  sample). Cap the tube and mix. The sample is now ready  for  analysis  (Section  1.3).  Allowance for sample dilution should be made in the calculations.  (If  mercury  is  to  be  deter- mined, a separate aliquot must be addition- ally acidified to contain 1%  (v/v)  HCl  to match the signal response of mercury in the calibration standard and reduce memory in- terference  effects.  Section  1.9).

NOTE: If a precipitate is formed during acidification, transport, or storage, the sam- ple aliquot must be treated using the proce- dure  described  in  Sections  11.2.2  through

11.2.7 prior to analysis.

  - Aqueous Sample Preparation—Total Recoverable Analytes

    - For the ‘‘direct analysis’’ of total recoverable analytes in drinking water sam- ples containing turbidity <1 NTU, treat an unfiltered acid preserved sample aliquot using the sample preparation procedure de- scribed in Section 11.1.1 while making allow- ance for sample dilution in the data calcula- tion (Section 1.2). For the determination of total recoverable analytes in all other aque- ous samples or for preconcentrating drinking water samples prior to analysis follow the procedure given in Sections 11.2.2 through 11.2.7.

    - For the determination of total re- coverable analytes in aqueous samples (other than drinking water with <1 NTU turbidity), transfer a 100 mL (1 mL) aliquot from a well mixed, acid preserved sample to a 250 mL Griffin beaker (Sections 1.2, 1.3, 1.6, 1.7, 1.8, and 1.9). (When necessary, smaller sample al- iquot volumes may be used.)

NOTE: If the sample contains undissolved solids >1%, a well mixed, acid preserved ali- quot containing no more than 1 g particulate material should be cautiously evaporated to near 10 mL and extracted using the acid-mix- ture procedure described in Sections 11.3.3 through 11.3.6.

    - Add 2 mL (1 + 1) nitric acid and 1.0 mL of (1 + 1) hydrochloric acid to the beaker containing the measured volume of  sample. Place the beaker on the hot plate for  solu- tion evaporation. The hot plate should be lo- cated in a fume hood and previously adjusted to provide evaporation at a temperature of approximately but no higher than 85  C.  (See the following note.) The beaker should be covered with an elevated  watch  glass  or other necessary steps should be taken to pre- vent sample contamination from the  fume hood   environment.

#### Environmental Protection Agency	Pt. 136, App. C

NOTE: For proper heating adjust the tem- perature control of the hot  plate  such  that an uncovered Griffin beaker containing 50 mL of water placed in the center of the hot plate can be maintained at a temperature ap- proximately but no higher than 85 C. (Once the beaker is covered with a watch glass the temperature of the water will rise to ap- proximately 95 C.)

    - Reduce the volume of the sample al- iquot to about 20 mL by gentle heating at 85

C. DO NOT BOIL. This step takes about two hours for a 100 mL aliquot with the rate of evaporation rapidly increasing as the sample volume approaches 20 mL. (A spare beaker containing 20 mL of water can be used as a gauge.)

    - Cover the lip of the beaker with a watch glass to reduce additional evaporation and gently reflux the sample for 30 minutes. (Slight boiling may  occur, but vigorous  boil- ing must be avoided to prevent loss of the HCl-H2O azeotrope.)

    - Allow  the  beaker  to  cool.  Quan-

titatively transfer the sample solution to a

50 mL volumetric  flask,  make  to  volume with reagent water, stopper and mix.

    - Allow any undissolved material to settle overnight, or centrifuge a portion of the prepared sample until clear. (If after centrifuging or standing overnight the sam- ple contains suspended solids that would clog the nebulizer, a portion of the sample may be filtered for their removal prior to analysis. However, care should be exercised to avoid potential contamination from filtration.) The sample is now ready for analysis. Be- cause the effects of various matrices on the stability of diluted samples cannot be char- acterized, all analyses should be performed as soon as possible after the completed prep- aration.

11.3    Solid Sample Preparation—Total Recoverable  Analytes

    - For the determination of total re- coverable analytes in solid samples, mix the sample thoroughly and transfer  a  portion (>20 g) to tared weighing dish, weigh the sample and record the wet weight (WW). (For samples with <35% moisture a 20 g portion is sufficient. For samples with moisture >35% a larger aliquot 50–100 g is required.) Dry the sample to a constant weight at 60 C and record the dry weight (DW) for calculation of percent solids (Section 12.6). (The sample is dried at 60 C to prevent the loss of mercury and other possible volatile metallic com- pounds, to facilitate sieving, and to  ready the sample for grinding.)

    - To achieve homogeneity, sieve the dried sample using a 5-mesh polypropylene sieve and grind in a mortar and pestle. (The sieve, mortar and pestle should be cleaned between samples.) From the dried, ground material  weigh  accurately  a  representative

1.0 0.01 g aliquot (W) of the sample and transfer to a 250 mL Phillips beaker for acid extraction (Sections 1.6, 1.7, 1.8, and 1.9).

    - To the beaker add 4 mL of (1 + 1) HNO3 and 10 mL of (1 + 4) HCl. Cover the lip of the beaker with a watch glass. Place the beaker on a hot plate for reflux extraction of the analytes. The hot plate should be located in a fume hood and previously adjusted to provide a reflux temperature of approxi- mately 95 C. (See the following note.)

NOTE: For proper heating adjust the tem- perature control of the hot  plate  such  that an uncovered Griffin beaker containing 50 mL of water placed in the center of the hot plate can be maintained at a temperature ap- proximately but no higher than 85 C. (Once the beaker is covered with a watch glass the temperature of the water will rise to ap- proximately 95 C.) Also, a block digester ca- pable of maintaining a temperature of 95 C and equipped with 250 mL constricted volu- metric digestion tubes may be substituted for the  hot  plate and  conical  beakers in  the extraction  step.

    - Heat  the  sample  and  gently  reflux for  30  minutes.  Very  slight  boiling   may occur, however vigorous boiling must be avoided to prevent loss of the HCl-H2O azeotrope. Some solution  evaporation  will occur (3–4 mL).

    - Allow the sample to cool and quan- titatively transfer the extract to a 100 mL volumetric flask. Dilute to volume with rea- gent water, stopper and mix.

    - Allow the sample extract  solution to stand overnight to separate insoluble ma- terial or centrifuge a portion of the sample solution until clear. (If after centrifuging or standing overnight the extract solution con- tains suspended solids that would clog the nebulizer, a portion of the extract solution may be filtered for their removal prior to analysis. However, care should be exercised to avoid potential contamination from fil- tration.) The sample extract is now ready for analysis. Because the effects of various mat- rices on the stability of diluted samples can- not be characterized, all analyses should be performed as soon as possible after the com- pleted preparation.

11.4   Sample Analysis

    - Prior to daily calibration of the in- strument inspect the sample introduction system including the nebulizer, torch, injec- tor tube and uptake tubing for salt deposits, dirt and debris that would restrict solution flow and affect instrument performance. Clean the system when needed or on a daily basis.

    - Configure the instrument system to the selected power and operating conditions as determined in Sections 10.1 and 10.2.

    - The instrument must be allowed to become thermally stable before calibration

#### Pt. 136, App. C

and analyses. This usually requires at least

30 to 60  minutes of  operation. After  instru- ment warmup, complete any required optical profiling or alignment particular to the in- strument.

    - For initial and daily operation cali- brate the instrument according to the in- strument manufacturer’s recommended pro- cedures, using mixed calibration standard so- lutions (Section 7.9) and the calibration blank (Section 7.10.1). A peristaltic  pump must be used to introduce all  solutions  to the nebulizer. To allow equilibrium to be reached in the plasma, aspirate all solutions for 30 seconds after reaching the plasma be- fore beginning integration of the background corrected signal to accumulate data. When possible, use the average value of replicate integration periods of the signal to be cor- related to the analyte concentration. Flush the system with the rinse blank (Section 7.10.4) for a minimum of 60 seconds (Section 4.4) between each standard. The calibration line should consist of a minimum of a cali- bration blank and a high standard. Rep- licates of the blank and highest standard provide an optimal distribution of calibra- tion standards to minimize the confidence band for a straight-line calibration in a re- sponse region with uniform variance.20

    - After completion of the initial re- quirements of this method (Sections 10.3 and 10.4), samples should be analyzed in the same operational manner used in the calibration routine with the rinse blank also being used between all sample solutions, LFBs, LFMs, and check solutions (Section 7.10.4).

    - During the analysis of samples, the laboratory must comply with the required quality control described in Sections 9.3 and

9.4. Only for the determination of dissolved analytes or the ‘‘direct analysis’’ of drinking water with turbidity of <1 NTU is the sample digestion step of the LRB, LFB, and  LFM not required.

#### 40 CFR Ch. I (7–1–17 Edition)

    - Determined sample analyte con- centrations that are 90% or more of the upper limit of the analyte LDR must be di- luted with reagent water that has been acidi- fied in the same manner as calibration blank and reanalyzed (see Section 11.4.8). Also, for the interelement spectral interference cor- rection routines to remain valid during sam- ple analysis, the interferant concentration must not exceed its LDR. If the interferant LDR is exceeded, sample dilution with acidi- fied reagent water and reanalysis is required. In these circumstances analyte detection limits are raised and determination by an- other approved test procedure that is either more sensitive and/or interference free is recommended.

    - When it is necessary to assess an op- erative matrix interference (e.g., signal re- duction due to high dissolved solids), the tests described in Section 9.5 are rec- ommended.

    - Report data as directed in Section 12.0.

11.5 If the method of standard additions (MSA) is used, standards are added at one or more levels to portions of a prepared sample. This technique 21 compensates for enhance- ment or depression of an analyte signal by a matrix. It will not correct for additive inter- ferences such as contamination, interele- ment interferences, or baseline shifts. This technique is valid in the linear range when the interference effect is constant over the range, the added analyte responds the same as the endogenous analyte, and the signal is corrected for additive interferences. The simplest version of this technique is the sin- gle-addition method. This procedure calls for two identical aliquots of the sample solution to be taken. To the first aliquot, a small vol- ume of standard is added; while to the second aliquot, a volume of acid blank is added equal to the standard addition. The sample concentration is calculated by the following:

where:

C = Concentration of the standard solution (mg/L)

S1 = Signal for fortified aliquot  S2 = Signal for unfortified aliquot

V1 = Volume of the standard addition (L)

V2  = Volume of the sample aliquot (L) used for MSA

For more than one fortified portion of the prepared sample, linear regression analysis can be applied using a computer or calcu- lator program to obtain the concentration of

the sample solution. An alternative to using the method of standard additions is use of the internal standard technique by adding one or more elements (not in the samples and verified not to cause an uncorrected interelement spectral interference) at the same concentration (which is sufficient for optimum precision) to the prepared samples (blanks and standards) that are affected the same as the analytes by the sample matrix. Use the ratio of analyte signal to the inter- nal standard signal for calibration and quan- titation.

#### Environmental Protection Agency	Pt. 136, App. C

12.0   Data Analysis and Calculations

  - Sample data should be reported in units of mg/L for aqueous samples and mg/kg dry weight for solid samples.

  - For dissolved aqueous analytes (Sec- tion 11.1) report the data generated directly from the instrument with allowance for sam- ple dilution. Do not report analyte con- centrations below the IDL.

  - For   total   recoverable   aqueous analytes (Section 11.2), multiply solution analyte  concentrations  by  the  dilution  fac- tor 0.5, when 100 mL aliquot is used  to produce the 50 mL final solution, and report data as instructed in Section 12.4. If a dif- ferent aliquot volume other than 100 mL is used for sample preparation, adjust the dilu- tion  factor   accordingly.   Also,   account   for any additional dilution of the prepared  sam- ple solution needed to complete the deter- mination of analytes exceeding  90%  or  more of  the  LDR  upper  limit.  Do  not  report  data

below the determined analyte MDL con- centration or below an adjusted detection limit reflecting smaller sample aliquots used in processing or additional dilutions required to complete the analysis.

  - For analytes with MDLs <0.01 mg/L, round the data values  to  the  thousandth place and report analyte  concentrations  up to three significant figures.  For  analytes with MDLs <0.01 mg/L round the data values to the 100th place and report analyte con- centrations up to three significant figures. Extract concentrations for solids data should be rounded in a similar manner before cal- culations in Section 12.5 are performed.

  - For total recoverable analytes in solid samples (Section 11.3), round the solu- tion analyte concentrations (mg/L) as in- structed in Section 12.4. Report the data up to three significant figures as mg/kg dry- weight basis unless specified otherwise by the program or data user. Calculate the con- centration using the equation below:

where:

C = Concentration in extract (mg/L)

V = Volume of extract (L, 100 mL = 0.1L) D = Dilution factor (undiluted = 1)

W = Weight of sample aliquot extracted (g 

0.001 = kg)

Do not report analyte data below the esti- mated solids MDL or an adjusted MDL be- cause of additional dilutions required to complete the analysis.

  - To report percent solids in solid sam- ples (Section 11.3) calculate as follows:

where:

DW = Sample weight (g) dried at 60 ßC WW = Sample weight (g) before drying

Note: If the data user, program or labora- tory requires that the reported  percent  sol- ids be determined by drying at 105 C, repeat the procedure given in Section 11.3 using a separate portion (>20 g) of the sample  and dry to constant weight at 103–105 C.

  - The QC data obtained during the analyses provide an indication of the quality of the sample data and should be provided with the sample results.

13.0   Method Performance

  - Listed in Table 4 are typical single laboratory total recoverable MDLs deter- mined for the recommended wavelengths using simultaneous ICP–AES and the oper- ating conditions given in Table 5. The MDLs

were determined in reagent blank  matrix (best case situation). PTFE  beakers  were used to avoid boron and silica contamination from glassware with the final dilution to 50 mL completed in polypropylene centrifuged tubes. The listed MDLs for solids are esti- mates and were calculated from the aqueous MDL   determinations.

  - Data obtained from single laboratory method testing are summarized in Table  6 for five types of water samples consisting of drinking water, surface water, ground water, and two wastewater effluents. The data pre- sented cover all analytes except cerium and titanium. Samples were prepared using the procedure described in Section 11.2. For each matrix, five replicate aliquots were prepared, analyzed and the average of the five deter- minations used to define the sample back- ground concentration of each analyte. In ad- dition, two pairs of duplicates were fortified

#### Pt. 136, App. C

at different concentration levels. For each method analyte, the sample background con- centration, mean percent recovery, standard deviation of the percent recovery, and rel- ative percent difference between the dupli- cate fortified samples are listed in Table 6. The variance of the five replicate sample background determinations is included in the calculated standard deviation of the per- cent recovery when the analyte concentra- tion in the sample was greater than the MDL. The tap and well waters were proc- essed in Teflon and quartz beakers and di- luted in polypropylene centrifuged tubes. The nonuse of borosilicate glassware is re- flected in the precision and recovery data for boron and silica in those two sample types.

  - Data obtained from single laboratory method  testing  are  summarized  in  Table   7 for three solid samples consisting of EPA 884 Hazardous Soil,  SRM  1645  River  Sediment, and EPA 286 Electroplating Sludge. Samples were prepared using the  procedure  described in Section 11.3. For each method analyte, the sample background concentration, mean per- cent recovery of the fortified additions, the standard deviation  of  the  percent  recovery, and relative percent difference between du- plicate additions were determined  as  de- scribed in Section 13.2. Data  presented  are for all analytes except cerium, silica, and ti- tanium. Limited comparative data to other methods and SRM materials are presented in Reference 23 of Section 16.0.

  - Performance data for  aqueous solu- tions independent of sample preparation from a multilaboratory study are provided in Table 8.22

  - Listed in Table 9 are regression equa- tions for precision and bias for 25 analytes abstracted from EPA Method Study 27, a multilaboratory  validation  study  of  Method

200.7.1 These equations were developed from data received from 12 laboratories using the total recoverable sample preparation proce- dure on reagent water, drinking water, sur- face water and three industrial effluents. For a complete review and description of the study, see Reference 16 of Section 16.0.

14.0    Pollution Prevention

  - Pollution prevention encompasses any technique that reduces or eliminates the quantity or toxicity of waste at the point of generation. Numerous opportunities for pol- lution prevention exist in laboratory  oper- ation. The EPA has established a preferred hierarchy of environmental management techniques that places pollution prevention as the management option of first choice. Whenever feasible, laboratory personnel should use pollution prevention techniques to address their waste generation (e.g., Sec- tion 7.8). When wastes cannot be feasibly re- duced at the source, the Agency recommends recycling as the next best option.

#### 40 CFR Ch. I (7–1–17 Edition)

  - For information about pollution pre- vention that may be applicable to labora- tories and research institutions, consult ‘‘Less is Better: Laboratory Chemical Man- agement for Waste Reduction’’, available from the American Chemical Society’s De- partment of Government Relations and Science Policy, 1155 16th Street NW., Wash- ington, DC 20036, (202) 872–4477.

15.0    Waste Management

15.1 The Environmental  Protection  Agen- cy requires that laboratory waste manage- ment practices be conducted consistent with all applicable rules and regulations. The Agency urges laboratories to protect the air, water, and land by minimizing and control- ling all releases from hoods and bench oper- ations, complying with the  letter  and  spirit of any sewer discharge permits and regula- tions, and by complying with all solid and hazardous  waste  regulations,   particularly the hazardous waste identification rules and land disposal restrictions. For further infor- mation on waste management consult ‘‘The Waste Management Manual for Laboratory Personnel’’, available from the American Chemical Society at the address listed in the Section 14.2.

16.0   References

- U.S. Environmental Protection Agency. Inductively Coupled Plasma—Atomic Emission  Spectrometric   Method   for Trace Element Analysis of Water and Wastes—Method 200.7, Dec. 1982. EPA–600/ 4–79–020, revised March 1983.

- U.S. Environmental Protection Agency. Inductively Coupled Plasma Atomic Emission Spectroscopy Method 6010, SW– 846 Test Methods for Evaluating Solid Waste, 3rd Edition, 1986.

- U.S. Environmental Protection Agency. Method 200.7: Determination of  Metals and Trace Elements in Water and Wastes by Inductively Coupled Plasma—Atomic Emission  Spectrometry,   revision   3.3, EPA 600 4–91/010, June 1991.

- U.S. Environmental Protection Agency. Inductively Coupled Plasma—Atomic Emission Spectrometry Method for the Analysis of Waters and Solids, EMMC, July 1992.

- Fassel, V.A. et al. Simultaneous Deter- mination of Wear Metals in Lubricating Oils by Inductively-Coupled Plasma Atomic Emission Spectrometry. Anal. Chem. 48:516–519, 1976.

- Merryfield, R.N. and R.C. Loyd. Simulta- neous Determination of Metals in Oil by Inductively Coupled Plasma Emission Spectrometry. Anal. Chem. 51:1965–1968, 1979.

- Winge, R.K. et al. Inductively Coupled Plasma—Atomic Emission Spectroscopy:

#### Environmental Protection Agency	Pt. 136, App. C

An Atlas of Spectral Information, Phys- ical Science Data 20. Elsevier Science Publishing, New York, New York, 1985.

- Boumans, P.W.J.M. Line Coincidence  Ta- bles for Inductively Coupled Plasma Atomic Emission Spectrometry, 2nd edi- tion. Pergamon Press, Oxford, United Kingdom, 1984.

- Carcinogens—Working With Carcinogens, Department of Health, Education, and Welfare, Public  Health  Service,  Center for Disease  Control,  National  Institute for Occupational Safety and Health, Pub- lication No. 77–206, Aug. 1977. Available from the National Technical Information Service (NTIS) as PB–277256.

- OSHA Safety and Health Standards, Gen- eral Industry, (29 CFR 1910), Occupa- tional Safety and Health Administration, OSHA 2206, (Revised, January 1976).

- Safety in Academic Chemistry Labora- tories, American Chemical Society Pub- lication, Committee on Chemical Safety, 3rd Edition, 1979.

- Proposed OSHA Safety and Health Stand- ards, Laboratories, Occupational Safety and Health Administration, FEDERAL REGISTER, July 24, 1986.

- Rohrbough, W.G. et al. Reagent Chemi- cals, American Chemical Society Speci- fications, 7th edition.  American  Chem- ical Society, Washington, DC, 1986.

- American Society for Testing and Mate- rials. Standard Specification for Reagent Water, D1193–77. Annual Book of ASTM Standards, Vol. 11.01. Philadelphia, PA, 1991.

- Code of Federal Regulations 40, Ch. 1, Pt. 136 Appendix B.

- Maxfield, R. and B. Mindak. EPA Method Study 27, Method 200.7 Trace Metals by

ICP, Nov. 1983. Available from National Technical  Information  Service  (NTIS)   as PB 85–248–656.

- Botto, R.I. Quality Assurance in  Oper- ating a Multielement ICP Emission Spec- trometer. Spectrochim. Acta, 39B(1):95– 113, 1984.

- Wallace, G.F.,  Some  Factors  Affecting the Performance of an ICP Sample Intro- duction System. Atomic Spectroscopy, Vol. 4, p. 188–192, 1983.

- Koirtyohann, S.R. et al. Nomenclature System for  the  Low-Power  Argon  Induc- tively Coupled Plasma, Anal. Chem. 52:1965, 1980.

- Deming, S.N. and S.L. Morgan. Experi- mental Design for Quality and Produc- tivity in Research, Development, and Manufacturing, Part III, pp. 119–123. Short course publication by Statistical Designs, 9941 Rowlett, Suite 6, Houston, TX 77075, 1989.

- Winefordner, J.D., Trace Analysis: Spectroscopic Methods for Elements, Chemical Analysis, Vol. 46, pp. 41–42.

- Jones,  C.L.  et  al.  An  Interlaboratory Study of Inductively Coupled Plasma Atomic Emission Spectroscopy Method 6010 and Digestion Method 3050. EPA–600/ 4–87–032, U.S. Environmental Protection Agency,  Las  Vegas,  Nevada,  1987.

- Martin, T.D., E.R. Martin and SE. Long. Method 200.2: Sample Preparation Proce- dure for Spectrochemical Analyses of Total Recoverable  Elements,  EMSL   ORD, USEPA, 1989.

17.0   Tables, Diagrams, Flowcharts, and Validation Data

TABLE 1—WAVELENGTHS, ESTIMATED INSTRUMENT DETECTION LIMITS, AND RECOMMENDED CALIBRATION

| Analyte | Wavelengtha (nm) | Estimated detection limitb (g/L) | Calibratec to (mg/L) |
| --- | --- | --- | --- |
| Aluminum ............................................................................................... | 308.215 | 45 | 10 |
| Antimony ................................................................................................ | 206.833 | 32 | 5 |
| Arsenic ................................................................................................... | 193.759 | 53 | 10 |
| Barium ................................................................................................... | 493.409 | 2.3 | 1 |
| Beryllium ................................................................................................ | 313.042 | 0.27 | 1 |
| Boron ..................................................................................................... | 249.678 | 5.7 | 1 |
| Cadmium ............................................................................................... | 226.502 | 3.4 | 2 |
| Calcium .................................................................................................. | 315.887 | 30 | 10 |
| Cerium ................................................................................................... | 413.765 | 48 | 2 |
| Chromium .............................................................................................. | 205.552 | 6.1 | 5 |
| Cobalt .................................................................................................... | 228.616 | 7.0 | 2 |
| Copper ................................................................................................... | 324.754 | 5.4 | 2 |
| Iron ........................................................................................................ | 259.940 | 6.2 | 10 |
| Lead ....................................................................................................... | 220.353 | 42 | 10 |
| Lithium ................................................................................................... | 670.784 | d 3.7 | 5 |
| Magnesium ............................................................................................ | 279.079 | 30 | 10 |
| Manganese ............................................................................................ | 257.610 | 1.4 | 2 |
| Mercury .................................................................................................. | 194.227 | 2.5 | 2 |
| Molybdenum .......................................................................................... | 203.844 | 12 | 10 |
| Nickel ..................................................................................................... | 231.604 | 15 | 2 |
| Phosphorus ........................................................................................... | 214.914 | 76 | 10 |
| Potassium .............................................................................................. | 766.491 | e 700 | 20 |

#### Pt. 136, App. C

40 CFR Ch. I (7–1–17 Edition)

TABLE 1—WAVELENGTHS, ESTIMATED INSTRUMENT DETECTION LIMITS, AND RECOMMENDED

CALIBRATION—Continued

| Analyte | Wavelengtha (nm) | Estimated detection limitb (g/L) | Calibratec to (mg/L) |
| --- | --- | --- | --- |
| Selenium ................................................................................................ | 196.090 | 75 | 5 |
| Silica (SiO2) ........................................................................................... | 251.611 | d 26 (SiO2) | 10 |
| Silver ...................................................................................................... | 328.068 | 7.0 | 0.5 |
| Sodium .................................................................................................. | 588.995 | 29 | 10 |
| Strontium ............................................................................................... | 421.552 | 0.77 | 1 |
| Thallium ................................................................................................. | 190.864 | 40 | 5 |
| Tin .......................................................................................................... | 189.980 | 25 | 4 |
| Titanium ................................................................................................. | 334.941 | 3.8 | 10 |
| Vanadium .............................................................................................. | 292.402 | 7.5 | 2 |
| Zinc ........................................................................................................ | 213.856 | 1.8 | 5 |

a The wavelengths listed are recommended because of their sensitivity and overall acceptability. Other wavelengths may be substituted if they can provide the needed sensitivity and are treated with the same corrective techniques for spectral inter- ference (see Section 4.1).

b These estimated 3-sigma instrumental detection limits 16 are provided only as a guide to instrumental limits. The method de- tection limits are sample dependent and may vary as the sample matrix varies. Detection limits for solids can be estimated by di- viding these values by the grams extracted per liter, which depends upon the extraction procedure. Divide solution detection lim- its by 10 for 1 g extracted to 100 mL for solid detection limits.

c Suggested concentration for instrument calibration.2 Other calibration limits in the linear ranges may be used.

d Calculated from 2-sigma data.5

e Highly dependent on operating conditions and plasma position.

TABLE 2—ON-LINE METHOD INTERELEMENT SPECTRAL   INTERFERANCES   ARISING   FROM INTERFERANTS AT THE 100 MG/L LEVEL

TABLE 3—MIXED STANDARD SOLUTIONS

| Solu- tion | Analytes |
| --- | --- |
| I ....... | Ag, As, B, Ba, Ca, Cd, Cu, Mn, Sb, and Se |
| II ...... | K, Li, Mo, Na, Sr, and Ti |
| III ..... | Co, P, V, and Ce |
| IV .... | Al, Cr, Hg, SiO2, Sn, and Zn |
| V ..... | Be, Fe, Mg, Ni, Pb, and Tl |
| Analyte | Wave- length (nm) | Interferant* |
| Ag ................ | 328.068 | Ce, Ti, Mn |
| Al .................. | 308.215 | V, Mo, Ce, Mn |
| As ................. | 193.759 | V, Al, Co, Fe, Ni |
| B .................. | 249.678 | None |
| Ba ................ | 493.409 | None |
| Be ................ | 313.042 | V, Ce |
| Ca ................ | 315.887 | Co, Mo, Ce |
| Cd ................ | 226.502 | Ni, Ti, Fe, Ce |
| Ce ................ | 413.765 | None |
| Co ................ | 228.616 | Ti, Ba, Cd, Ni, Cr, Mo, Ce |
| Cr ................. | 205.552 | Be, Mo, Ni |
| Cu ................ | 324.754 | Mo, Ti |
| Fe ................. | 259.940 | None |
| Hg ................ | 194.227 | V, Mo |
| K .................. | 766.491 | None |
| Li .................. | 670.784 | None |
| Mg ................ | 279.079 | Ce |
| Mn ................ | 257.610 | Ce |
| Mo ................ | 203.844 | Ce |
| Na ................ | 588.995 | None |
| Ni ................. | 231.604 | Co, Tl |
| P .................. | 214.914 | Cu, Mo |
| Pb ................ | 220.353 | Co, Al, Ce, Cu, Ni, Ti, Fe |
| Sb ................ | 206.833 | Cr, Mo, Sn, Ti, Ce, Fe |
| Se ................ | 196.099 | Fe |
| SiO2 ............. | 251.611 | None |
| Sn ................ | 189.980 | Mo, Ti, Fe, Mn, Si |
| Sr ................. | 421.552 | None |
| Tl .................. | 190.864 | Ti, Mo, Co, Ce, Al, V, Mn |
| Ti .................. | 334.941 | None |
| V .................. | 292.402 | Mo, Ti, Cr, Fe, Ce |
| Zn ................. | 213.856 | Ni, Cu, Fe |

TABLE 4—TOTAL RECOVERABLE METHOD DETECTION LIMITS (MDL)

| Analyte | MDLs Aqueous, mg/L(1) | Solids, mg/kg(2) |
| --- | --- | --- |
| Ag ...................... | 0.002 | 0.3 |
| Al ....................... | 0.02 | 3 |
| As ...................... | 0.008 | 2 |
| B ........................ | 0.003 | — |
| Ba ...................... | 0.001 | 0.2 |
| Be ...................... | 0.0003 | 0.1 |
| Ca ...................... | 0.01 | 2 |
| Cd ...................... | 0.001 | 0.2 |
| Ce ...................... | 0.02 | 3 |
| Co ...................... | 0.002 | 0.4 |
| Cr ....................... | 0.004 | 0.8 |
| Cu ...................... | 0.003 | 0.5 |
| Fe ...................... | *0.03 | 6 |
| Hg ...................... | 0.007 | 2 |
| K ........................ | 0.3 | 60 |
| Li ........................ | 0.001 | 0.2 |
| Mg ...................... | 0.02 | 3 |
| Mn ...................... | 0.001 | 0.2 |
| Mo ...................... | 0.004 | 1 |
| Na ...................... | 0.03 | 6 |
| Ni ....................... | 0.005 | 1 |
| P ........................ | 0.06 | 12 |
| Pb ...................... | 0.01 | 2 |
| Sb ...................... | 0.008 | 2 |
| Se ...................... | 0.02 | 5 |
| SiO2 ................... | 0.02 | — |
| Sn ...................... | 0.007 | 2 |
| Sr ....................... | 0.0003 | 0.1 |
| Tl ........................ | 0.001 | 0.2 |
| Ti ........................ | 0.02 | 3 |
| V ........................ | 0.003 | 1 |

These on-line interferences from method analytes and tita- nium only were observed using an instrument with 0.035 nm resolution (see Section 4.1.2). Interferant ranked by mag- nitude of intensity with the most severe interferant listed first in the row.

#### Environmental Protection Agency	Pt. 136, App. C

TABLE 4—TOTAL RECOVERABLE METHOD DETECTION LIMITS (MDL)—Continued

TABLE 5—INDUCTIVELY COUPLED PLASMA INSTRUMENT OPERATING CONDITIONS

| Analyte | MDLs Aqueous, mg/L(1) | Solids, mg/kg(2) |
| --- | --- | --- |
| Zn ...................... | 0.002 | 0.3 |

Incident rf power .............................   1100 watts

Reflected rf power ..........................   <5 watts Viewing height above work coil ......   15 mm Injector tube orifice i.d. ...................   1 mm Argon supply ...................................   liquid argon

Argon pressure ...............................   40 psi Coolant argon flow rate ..................   19 L/min. Aerosol carrier argon flow rate .......   620 mL/min. Auxiliary (plasma) argon flow rate ..   300 mL/min. Sample uptake rate controlled to ...   1.2 mL/min.

(1) MDL concentrations are computed for original matrix with allowance for 2x sample preconcentration during preparation. Samples were processed in PTFE and diluted in 50-mL plas- tic centrifuge tubes.

(2) Estimated, calculated from aqueous MDL determinations.

— Boron not reported because of glassware contamination. Silica not determined in solid samples.

- Elevated value due to fume-hood contamination.

40 CFR Ch. I (7–1–17 Edition)

368

|  | Pond Water |  |
| --- | --- | --- |
| Ag ................................................................................... | <0.002 | 0.05 | 92 | 0.0 | 0.0 | 0.2 | 94 | 0.0 | 0.0 |
| Al .................................................................................... | 0.819 | 0.2 | 88 | 10.0 | 5.0 | 0.8 | 100 | 2.9 | 3.7 |
| As ................................................................................... | <0.008 | 0.05 | 102 | 0.0 | 0.0 | 0.2 | 98 | 1.4 | 4.1 |
| B ..................................................................................... | 0.034 | 0.1 | 111 | 8.9 | 6.9 | 0.4 | 103 | 2.0 | 0.0 |
| Ba ................................................................................... | 0.029 | 0.05 | 96 | 0.9 | 0.0 | 0.2 | 97 | 0.3 | 0.5 |
| Be ................................................................................... | <0.0003 | 0.01 | 95 | 0.4 | 1.1 | 0.2 | 95 | 0.0 | 0.0 |
| Ca ................................................................................... | 53.9 | 5.0 | * | * | 0.7 | 20.0 | 100 | 2.0 | 1.5 |
| Cd ................................................................................... | <0.001 | 0.01 | 107 | 0.0 | 0.0 | 0.1 | 97 | 0.0 | 0.0 |
| Co ................................................................................... | <0.002 | 0.02 | 100 | 2.7 | 7.5 | 0.2 | 97 | 0.7 | 2.1 |
| Cr ................................................................................... | <0.004 | 0.01 | 105 | 3.5 | 9.5 | 0.1 | 103 | 1.1 | 2.9 |

Pt. 136, App. C

TABLE 6—PRECISION AND RECOVERY DATA IN AQUEOUS MATRICES

| Analyte | Sample conc. mg/L | Low spike mg/L | Average recovery R (%) | S (R) | RPD | High spike mg/L | Average recovery R (%) | S (R) | RPD |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Tap Water

| Ag ................................................................................... | <0.002 | 0.05 | 95 | 0.7 | 2.1 | 0.2 | 96 | 0.0 | 0.0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Al .................................................................................... | 0.185 | 0.05 | 98 | 8.8 | 1.7 | 0.2 | 105 | 3.0 | 3.1 |
| As ................................................................................... | <0.008 | 0.05 | 108 | 1.4 | 3.7 | 0.2 | 101 | 0.7 | 2.0 |
| B ..................................................................................... | 0.023 | 0.1 | 98 | 0.2 | 0.0 | 0.4 | 98 | 0.2 | 0.5 |
| Ba ................................................................................... | 0.042 | 0.05 | 102 | 1.6 | 2.2 | 0.2 | 98 | 0.4 | 0.8 |
| Be ................................................................................... | <0.0003 | 0.01 | 100 | 0.0 | 0.0 | 0.1 | 99 | 0.0 | 0.0 |
| Ca ................................................................................... | 35.2 | 5.0 | 101 | 8.8 | 1.7 | 20.0 | 103 | 2.0 | 0.9 |
| Cd ................................................................................... | <0.001 | 0.01 | 105 | 3.5 | 9.5 | 0.1 | 98 | 0.0 | 0.0 |
| Co ................................................................................... | <0.002 | 0.02 | 100 | 0.0 | 0.0 | 0.2 | 99 | 0.5 | 1.5 |
| Cr ................................................................................... | <0.004 | 0.01 | 110 | 0.0 | 0.0 | 0.1 | 102 | 0.0 | 0.0 |
| Cu ................................................................................... | <0.003 | 0.02 | 103 | 1.8 | 4.9 | 0.2 | 101 | 1.2 | 3.5 |
| Fe ................................................................................... | 0.008 | 0.1 | 106 | 1.0 | 1.8 | 0.4 | 105 | 0.3 | 0.5 |
| Hg ................................................................................... | <0.007 | 0.05 | 103 | 0.7 | 1.9 | 0.2 | 100 | 0.4 | 1.0 |
| K ..................................................................................... | 1.98 | 5.0 | 109 | 1.4 | 2.3 | 20. | 107 | 0.7 | 1.7 |
| Li .................................................................................... | 0.006 | 0.02 | 103 | 6.9 | 3.8 | 0.2 | 110 | 1.9 | 4.4 |
| Mg .................................................................................. | 8.08 | 5.0 | 104 | 2.2 | 1.5 | 20.0 | 100 | 0.7 | 1.1 |
| Mn .................................................................................. | <0.001 | 0.01 | 100 | 0.0 | 0.0 | 0.1 | 99 | 0.0 | 0.0 |
| Mo .................................................................................. | <0.004 | 0.02 | 95 | 3.5 | 10.5 | 0.2 | 108 | 0.5 | 1.4 |
| Na ................................................................................... | 10.3 | 5.0 | 99 | 3.0 | 2.0 | 20.0 | 106 | 1.0 | 1.6 |
| Ni .................................................................................... | <0.005 | 0.02 | 108 | 1.8 | 4.7 | 0.2 | 104 | 1.1 | 2.9 |
| P ..................................................................................... | 0.045 | 0.1 | 102 | 13.1 | 9.4 | 0.4 | 104 | 3.2 | 1.3 |
| Pb ................................................................................... | <0.01 | 0.05 | 95 | 0.7 | 2.1 | 0.2 | 100 | 0.2 | 0.5 |
| Sb ................................................................................... | <0.008 | 0.05 | 99 | 0.7 | 2.0 | 0.2 | 102 | 0.7 | 2.0 |
| Se ................................................................................... | <0.02 | 0.1 | 87 | 1.1 | 3.5 | 0.4 | 99 | 0.8 | 2.3 |
| SiO2 ................................................................................ | 6.5 | 5.0 | 104 | 3.3 | 3.4 | 20.0 | 96 | 1.1 | 2.3 |
| Sn ................................................................................... | <0.007 | 0.05 | 103 | 2.1 | 5.8 | 0.2 | 101 | 1.8 | 5.0 |
| Sr .................................................................................... | 0.181 | 0.1 | 102 | 3.3 | 2.1 | 0.4 | 105 | 0.8 | 1.0 |
| Tl .................................................................................... | <0.02 | 0.1 | 101 | 3.9 | 10.9 | 0.4 | 101 | 0.1 | 0.3 |
| V ..................................................................................... | <0.003 | 0.05 | 101 | 0.7 | 2.0 | 0.2 | 99 | 0.2 | 0.5 |
| Zn ................................................................................... | 0.005 | 0.05 | 101 | 3.7 | 9.0 | 0.2 | 98 | 0.9 | 2.5 |

Environmental Protection Agency

Pt. 136, App. C

369

| Cu ................................................................................... | <0.003 | 0.02 | 98 | 2.1 | 4.4 | 0.2 | 100 | 0.5 | 1.5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Fe ................................................................................... | 0.875 | 0.2 | 95 | 8.9 | 2.8 | 0.8 | 97 | 3.2 | 3.6 |
| Hg ................................................................................... | <0.007 | 0.05 | 97 | 3.5 | 10.3 | 0.2 | 98 | 0.0 | 0.0 |
| K ..................................................................................... | 2.48 | 5.0 | 106 | 0.3 | 0.1 | 20.0 | 103 | 0.2 | 0.4 |
| Li .................................................................................... | <0.001 | 0.02 | 110 | 0.0 | 0.0 | 0.2 | 106 | 0.2 | 0.5 |
| Mg .................................................................................. | 10.8 | 5.0 | 102 | 0.5 | 0.0 | 20.0 | 96 | 0.7 | 1.3 |
| Mn .................................................................................. | 0.632 | 0.01 | * | * | 0.2 | 0.1 | 97 | 2.3 | 0.3 |
| Mo .................................................................................. | <0.004 | 0.02 | 105 | 3.5 | 9.5 | 0.2 | 103 | 0.4 | 1.0 |
| Na ................................................................................... | 17.8 | 5.0 | 103 | 1.3 | 0.4 | 20.0 | 94 | 0.3 | 0.0 |
| Ni .................................................................................... | <0.005 | 0.02 | 96 | 5.6 | 9.1 | 0.2 | 100 | 0.7 | 1.5 |
| P ..................................................................................... | 0.196 | 0.1 | 91 | 14.7 | 0.3 | 0.4 | 108 | 3.9 | 1.3 |
| Pb ................................................................................... | <0.01 | 0.05 | 96 | 2.6 | 7.8 | 0.2 | 100 | 0.7 | 2.0 |
| Sb ................................................................................... | <0.008 | 0.05 | 102 | 2.8 | 7.8 | 0.2 | 104 | 0.4 | 1.0 |
| Se ................................................................................... | <0.02 | 0.1 | 104 | 2.1 | 5.8 | 0.4 | 103 | 1.6 | 4.4 |
| SiO2 ................................................................................ | 7.83 | 5.0 | 151 | 1.6 | 1.3 | 20.0 | 117 | 0.4 | 0.6 |
| Sn ................................................................................... | <0.007 | 0.05 | 98 | 0.0 | 0.0 | 0.2 | 99 | 1.1 | 3.0 |
| Sr .................................................................................... | 0.129 | 0.1 | 105 | 0.4 | 0.0 | 0.4 | 99 | 0.1 | 0.2 |
| Tl .................................................................................... | <0.02 | 0.1 | 103 | 1.1 | 2.9 | 0.4 | 97 | 1.3 | 3.9 |
| V ..................................................................................... | 0.003 | 0.05 | 94 | 0.4 | 0.0 | 0.2 | 98 | 0.1 | 0.0 |
| Zn ................................................................................... | 0.006 | 0.05 | 97 | 1.6 | 1.8 | 0.2 | 94 | 0.4 | 0.0 |
|  |  |  | Well Water |  |  |  |  |  |  |
| Ag ................................................................................... | <0.002 | 0.05 | 97 | 0.7 | 2.1 | 0.2 | 96 | 0.2 | 0.5 |
| Al .................................................................................... | 0.036 | 0.05 | 107 | 7.6 | 10.1 | 0.2 | 101 | 1.1 | 0.8 |
| As ................................................................................... | <0.008 | 0.05 | 107 | 0.7 | 1.9 | 0.2 | 104 | 0.4 | 1.0 |
| B ..................................................................................... | 0.063 | 0.1 | 97 | 0.6 | 0.7 | 0.4 | 98 | 0.8 | 2.1 |
| Ba ................................................................................... | 0.102 | 0.05 | 102 | 3.0 | 0.0 | 0.2 | 99 | 0.9 | 1.0 |
| Be ................................................................................... | <0.0003 | 0.01 | 100 | 0.0 | 0.0 | 0.1 | 100 | 0.0 | 0.0 |
| Ca ................................................................................... | 93.8 | 5.0 | * | * | 2.1 | 20.0 | 100 | 4.1 | 0.1 |
| Cd ................................................................................... | 0.002 | 0.01 | 90 | 0.0 | 0.0 | 0.1 | 96 | 0.0 | 0.0 |
| Co ................................................................................... | <0.002 | 0.02 | 94 | 0.4 | 1.1 | 0.2 | 94 | 0.4 | 1.1 |
| Cr ................................................................................... | <0.004 | 0.01 | 100 | 7.1 | 20.0 | 0.1 | 100 | 0.4 | 1.0 |
| Cu ................................................................................... | <0.005 | 0.02 | 100 | 1.1 | 0.4 | 0.2 | 96 | 0.5 | 1.5 |
| Fe ................................................................................... | 0.042 | 0.1 | 99 | 2.3 | 1.4 | 0.4 | 97 | 1.4 | 3.3 |
| Hg ................................................................................... | <0.007 | 0.05 | 94 | 2.8 | 8.5 | 0.2 | 93 | 1.2 | 3.8 |
| K ..................................................................................... | 6.21 | 5.0 | 96 | 3.4 | 3.6 | 20.0 | 101 | 1.2 | 2.3 |
| Li .................................................................................... | 0.001 | 0.02 | 100 | 7.6 | 9.5 | 0.2 | 104 | 1.0 | 1.9 |
| Mg .................................................................................. | 24.5 | 5.0 | 95 | 5.6 | 0.3 | 20.0 | 93 | 1.6 | 1.2 |
| Mn .................................................................................. | 2.76 | 0.01 | * | * | 0.4 | 0.1 | * | * | 0.7 |
| Mo .................................................................................. | <0.004 | 0.02 | 108 | 1.8 | 4.7 | 0.2 | 101 | 0.2 | 0.5 |
| Na ................................................................................... | 35.0 | 5.0 | 101 | 11.4 | 0.8 | 20.0 | 100 | 3.1 | 1.5 |
| Ni .................................................................................... | <0.005 | 0.02 | 112 | 1.8 | 4.4 | 0.2 | 96 | 0.2 | 0.5 |
| P ..................................................................................... | 0.197 | 0.1 | 95 | 12.7 | 1.9 | 0.4 | 98 | 3.4 | 0.9 |
| Pb ................................................................................... | <0.01 | 0.05 | 87 | 4.9 | 16.1 | 0.2 | 95 | 0.2 | 0.5 |
| Sb ................................................................................... | <0.008 | 0.05 | 98 | 2.8 | 8.2 | 0.2 | 99 | 1.4 | 4.0 |
| Se ................................................................................... | <0.02 | 0.1 | 102 | 0.4 | 1.0 | 0.4 | 94 | 1.1 | 3.4 |
| SiO2 ................................................................................ | 13.1 | 5.0 | 93 | 4.8 | 2.8 | 20.0 | 99 | 0.8 | 0.0 |
| Sn ................................................................................... | <0.007 | 0.05 | 98 | 2.8 | 8.2 | 0.2 | 94 | 0.2 | 0.5 |
| Sr .................................................................................... | 0.274 | 0.1 | 94 | 5.7 | 2.7 | 0.4 | 95 | 1.7 | 2.2 |

370

Pt. 136, App. C

TABLE 6—PRECISION AND RECOVERY DATA IN AQUEOUS MATRICES—Continued

| Analyte | Sample conc. mg/L | Low spike mg/L | Average recovery R (%) | S (R) | RPD | High spike mg/L | Average recovery R (%) | S (R) | RPD |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Tl .................................................................................... | <0.02 | 0.1 | 92 | 0.4 | 1.1 | 0.4 | 95 | 1.1 | 3.2 |
| V ..................................................................................... | <0.003 | 0.05 | 98 | 0.0 | 0.0 | 0.2 | 99 | 0.4 | 1.0 |
| Zn ................................................................................... | 0.538 | 0.05 | * | * | 0.7 | 0.2 | 99 | 2.5 | 1.1 |

Sewage Treatment Effluent

| Ag ................................................................................... | 0.009 | 0.05 | 92 | 1.5 | 3.6 | 0.2 | 95 | 0.1 | 0.0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Al .................................................................................... | 1.19 | 0.05 | * | * | 0.9 | 0.2 | 113 | 12.4 | 2.1 |
| As ................................................................................... | <0.008 | 0.05 | 99 | 2.1 | 6.1 | 0.2 | 93 | 2.1 | 6.5 |
| B ..................................................................................... | 0.226 | 0.1 | 217 | 16.3 | 9.5 | 0.4 | 119 | 13.1 | 20.9 |
| Ba ................................................................................... | 0.189 | 0.05 | 90 | 6.8 | 1.7 | 0.2 | 99 | 1.6 | 0.5 |
| Be ................................................................................... | <0.0003 | 0.01 | 94 | 0.4 | 1.1 | 0.1 | 100 | 0.4 | 1.0 |
| Ca ................................................................................... | 87.9 | 5.0 | * | * | 0.6 | 20.0 | 101 | 3.7 | 0.0 |
| Cd ................................................................................... | 0.009 | 0.01 | 89 | 2.6 | 2.3 | 0.1 | 97 | 0.4 | 1.0 |
| Co ................................................................................... | 0.016 | 0.02 | 95 | 3.1 | 0.0 | 0.2 | 93 | 0.4 | 0.5 |
| Cr ................................................................................... | 0.128 | 0.01 | * | * | 1.5 | 0.1 | 97 | 2.4 | 2.7 |
| Cu ................................................................................... | 0.174 | 0.02 | 98 | 33.1 | 4.7 | 0.2 | 98 | 3.0 | 1.4 |
| Fe ................................................................................... | 1.28 | 0.1 | * | * | 2.8 | 0.4 | 111 | 7.0 | 0.6 |
| Hg ................................................................................... | <0.007 | 0.05 | 102 | 1.4 | 3.9 | 0.2 | 98 | 0.5 | 1.5 |
| K ..................................................................................... | 10.6 | 5.0 | 104 | 2.8 | 1.3 | 20.0 | 101 | 0.6 | 0.0 |
| Li .................................................................................... | 0.011 | 0.02 | 103 | 8.5 | 3.2 | 0.2 | 105 | 0.8 | 0.5 |
| Mg .................................................................................. | 22.7 | 5.0 | 100 | 4.4 | 0.0 | 20.0 | 92 | 1.1 | 0.2 |
| Mn .................................................................................. | 0.199 | 0.01 | * | * | 2.0 | 0.1 | 104 | 1.9 | 0.3 |
| Mo .................................................................................. | 0.125 | 0.02 | 110 | 21.2 | 6.8 | 0.2 | 102 | 1.3 | 0.9 |
| Na ................................................................................... | 0.236 | 5.0 | * | * | 0.0 | 20.0 | * | * | 0.4 |
| Ni .................................................................................... | 0.087 | 0.02 | 122 | 10.7 | 4.5 | 0.2 | 98 | 0.8 | 1.1 |
| P ..................................................................................... | 4.71 | 0.1 | * | * | 2.6 | 0.4 | * | * | 1.4 |
| Pb ................................................................................... | 0.015 | 0.05 | 91 | 3.5 | 5.0 | 0.2 | 96 | 1.3 | 2.9 |
| Sb ................................................................................... | <0.008 | 0.05 | 97 | 0.7 | 2.1 | 0.2 | 103 | 1.1 | 2.9 |
| Se ................................................................................... | <0.02 | 0.1 | 108 | 3.9 | 10.0 | 0.4 | 101 | 2.6 | 7.2 |
| SiO2 ................................................................................ | 16.7 | 5.0 | 124 | 4.0 | 0.9 | 20.0 | 108 | 1.1 | 0.8 |
| Sn ................................................................................... | 0.016 | 0.05 | 90 | 3.8 | 0.0 | 0.2 | 95 | 1.0 | 0.0 |
| Sr .................................................................................... | 0.515 | 0.1 | 103 | 6.4 | 0.5 | 0.4 | 96 | 1.6 | 0.2 |
| Tl .................................................................................... | <0.02 | 0.1 | 105 | 0.4 | 1.0 | 0.4 | 95 | 0.0 | 0.0 |
| V ..................................................................................... | 0.003 | 0.05 | 93 | 0.9 | 2.0 | 0.2 | 97 | 0.2 | 0.5 |
| Zn ................................................................................... | 0.160 | 0.05 | 98 | 3.3 | 1.9 | 0.2 | 101 | 1.0 | 1.4 |

40 CFR Ch. I (7–1–17 Edition)

Industrial Effluent

| Ag ................................................................................... | <0.0003 | 0.05 | 88 | 0.0 | 0.0 | 0.2 | 84 | 0.9 | 3.0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Al .................................................................................... | 0.054 | 0.05 | 88 | 11.7 | 12.2 | 0.2 | 90 | 3.9 | 8.1 |
| As ................................................................................... | <0.02 | 0.05 | 82 | 2.8 | 9.8 | 0.2 | 88 | 0.5 | 1.7 |
| B ..................................................................................... | 0.17 | 0.1 | 162 | 17.6 | 13.9 | 0.4 | 92 | 4.7 | 9.3 |
| Ba ................................................................................... | 0.083 | 0.05 | 86 | 8.2 | 1.6 | 0.2 | 85 | 2.3 | 2.4 |
| Be ................................................................................... | <0.0006 | 0.01 | 94 | 0.4 | 1.1 | 0.1 | 82 | 1.4 | 4.9 |

371

| Ca ................................................................................... | 500 | 5.0 | * | * | 2.8 | 20.0 | * | * | 2.3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Cd ................................................................................... | 0.008 | 0.01 | 85 | 4.7 | 6.1 | 0.1 | 82 | 1.4 | 4.4 |
| Co ................................................................................... | <0.004 | 0.02 | 93 | 1.8 | 5.4 | 0.2 | 83 | 0.4 | 1.2 |
| Cr ................................................................................... | 0.165 | 0.01 | * | * | 4.5 | 0.1 | 106 | 6.6 | 5.6 |
| Cu ................................................................................... | 0.095 | 0.02 | 93 | 23.3 | 0.9 | 0.2 | 95 | 2.7 | 2.8 |
| Fe ................................................................................... | 0.315 | 0.1 | 88 | 16.4 | 1.0 | 0.4 | 99 | 6.5 | 8.0 |
| Hg ................................................................................... | <0.01 | 0.05 | 87 | 0.7 | 2.3 | 0.2 | 86 | 0.4 | 1.2 |
| K ..................................................................................... | 2.87 | 5.0 | 101 | 3.4 | 2.4 | 20.0 | 100 | 0.8 | 0.4 |
| Li .................................................................................... | 0.069 | 0.02 | 103 | 24.7 | 5.6 | 0.2 | 104 | 2.5 | 2.2 |
| Mg .................................................................................. | 6.84 | 5.0 | 87 | 3.1 | 0.0 | 20.0 | 87 | 0.9 | 1.2 |
| Mn .................................................................................. | 0.141 | 0.01 | * | * | 1.2 | 0.1 | 89 | 6.6 | 4.8 |
| Mo .................................................................................. | 1.27 | 0.02 | * | * | 0.0 | 0.2 | 100 | 15.0 | 2.7 |
| Na ................................................................................... | 1500 | 5.0 | * | * | 2.7 | 20.0 | * | * | 2.0 |
| Ni .................................................................................... | 0.014 | 0.02 | 98 | 4.4 | 3.0 | 0.2 | 87 | 0.5 | 1.1 |
| P ..................................................................................... | 0.326 | 0.1 | 105 | 16.0 | 4.7 | 0.4 | 97 | 3.9 | 1.4 |
| Pb ................................................................................... | 0.251 | 0.05 | 80 | 19.9 | 1.4 | 0.2 | 88 | 5.0 | 0.9 |
| Sb ................................................................................... | 2.81 | 0.05 | * | * | 0.4 | 0.2 | * | * | 2.0 |
| Se ................................................................................... | 0.021 | 0.1 | 106 | 2.6 | 3.2 | 0.4 | 105 | 1.9 | 4.6 |
| SiO2 ................................................................................ | 6.83 | 5.0 | 99 | 6.8 | 1.7 | 20.0 | 100 | 2.2 | 3.0 |
| Sn ................................................................................... | <0.01 | 0.05 | 87 | 0.7 | 2.3 | 0.2 | 86 | 0.4 | 1.2 |
| Sr .................................................................................... | 6.54 | 0.1 | * | * | 2.0 | 0.4 | * | * | 2.7 |
| Tl .................................................................................... | <0.03 | 0.1 | 87 | 1.8 | 5.8 | 0.4 | 84 | 1.1 | 3.6 |
| V ..................................................................................... | <0.005 | 0.05 | 90 | 1.4 | 4.4 | 0.2 | 84 | 1.1 | 3.6 |
| Zn ................................................................................... | 0.024 | 0.05 | 89 | 6.0 | 4.4 | 0.2 | 91 | 3.5 | 8.9 |

Environmental Protection Agency

S (R) Standard deviation of percent recovery.

RPD Relative percent difference between duplicate spike determinations.

<Sample concentration below established method detection limit.

* Spike concentration <10% of sample background concentration.

TABLE 7—PRECISION AND RECOVERY DATA IN SOLID MATRICES

| Analyte | Sample conc. mg/kg | Low + spike mg/kg | Average recovery R (%) | S (R) | RPD | High + spike mg/kg | Average recovery R (%) | S (R) | RPD |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Pt. 136, App. C

EPA Hazardous Soil #884

| Ag ................................................................................... | 1.1 | 20 | 98 | 0.7 | 1.0 | 100 | 96 | 0.2 | 0.6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Al .................................................................................... | 5080 | 20 | * | * | 7.2 | 100 | * | * | 5.4 |
| As ................................................................................... | 5.7 | 20 | 95 | 5.4 | 10.6 | 100 | 96 | 1.4 | 3.6 |
| B ..................................................................................... | 20.4 | 100 | 93 | 2.7 | 5.3 | 400 | 100 | 2.1 | 5.5 |
| Ba ................................................................................... | 111 | 20 | 98 | 71.4 | 22.2 | 100 | 97 | 10.0 | 1.0 |
| Be ................................................................................... | 0.66 | 20 | 97 | 0.7 | 2.3 | 100 | 99 | 0.1 | 0.2 |
| Ca ................................................................................... | 85200 | ¥ | ¥ | ¥ | ¥ | ¥ | ¥ | ¥ | ¥ |
| Cd ................................................................................... | 2 | 20 | 93 | 0.7 | 1.0 | 100 | 94 | 0.2 | 0.4 |
| Co ................................................................................... | 5.5 | 20 | 96 | 3.5 | 7.7 | 100 | 93 | 0.8 | 2.1 |
| Cr ................................................................................... | 79.7 | 20 | 87 | 28.8 | 16.5 | 100 | 104 | 1.3 | 1.1 |
| Cu ................................................................................... | 113 | 20 | 110 | 16.2 | 4.4 | 100 | 104 | 4.0 | 4.2 |
| Fe ................................................................................... | 16500 | ¥ | ¥ | ¥ | ¥ | ¥ | ¥ | ¥ | ¥ |
| Hg ................................................................................... | <1.4 | 10 | 92 | 2.5 | 7.7 | 40 | 98 | 0.0 | 0.0 |

372

Pt. 136, App. C

TABLE 7—PRECISION AND RECOVERY DATA IN SOLID MATRICES—Continued

| Analyte | Sample conc. mg/kg | Low + spike mg/kg | Average recovery R (%) | S (R) | RPD | High + spike mg/kg | Average recovery R (%) | S (R) | RPD |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| K ..................................................................................... | 621 | 500 | 121 | 1.3 | 0.0 | 2000 | 107 | 0.9 | 1.8 |
| Li .................................................................................... | 6.7 | 10 | 113 | 3.5 | 4.4 | 40 | 106 | 0.6 | 0.6 |
| Mg .................................................................................. | 24400 | 500 | * | * | 8.4 | 2000 | * | * | 10.1 |
| Mn .................................................................................. | 343 | 20 | * | * | 8.5 | 100 | 95 | 11.0 | 1.6 |
| Mo .................................................................................. | 5.3 | 20 | 88 | 5.3 | 13.2 | 100 | 91 | 1.4 | 4.1 |
| Na ................................................................................... | 195 | 500 | 102 | 2.2 | 2.4 | 2000 | 100 | 1.5 | 3.7 |
| Ni .................................................................................... | 15.6 | 20 | 100 | 1.8 | 0.0 | 100 | 94 | 1.5 | 3.6 |
| P ..................................................................................... | 595 | 500 | 106 | 13.4 | 8.0 | 2000 | 103 | 3.2 | 2.7 |
| Pb ................................................................................... | 145 | 20 | 88 | 51.8 | 17.9 | 100 | 108 | 15.6 | 17.4 |
| Sb ................................................................................... | 6.1 | 20 | 83 | 3.9 | 7.5 | 100 | 81 | 1.9 | 5.9 |
| Se ................................................................................... | <5 | 20 | 79 | 14.7 | 52.4 | 100 | 99 | 0.7 | 2.1 |
| Sn ................................................................................... | 16.6 | 20 | 91 | 34.6 | 5.8 | 80 | 112 | 8.7 | 2.8 |
| Sr .................................................................................... | 102 | 100 | 84 | 9.6 | 10.8 | 400 | 94 | 2.5 | 4.6 |
| Tl .................................................................................... | <4 | 20 | 92 | 4.8 | 14.6 | 100 | 91 | 1.5 | 4.6 |
| V ..................................................................................... | 16.7 | 20 | 104 | 4.2 | 5.4 | 100 | 99 | 0.8 | 1.7 |
| Zn ................................................................................... | 131 | 20 | 103 | 31.2 | 7.3 | 100 | 104 | 7.2 | 6.4 |

40 CFR Ch. I (7–1–17 Edition)

EPA Electroplating Sludge #286

| Ag ................................................................................... | 6 | 20 | 96 | 0.2 | 0.4 | 100 | 93 | 0.1 | 0.4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Al .................................................................................... | 4980 | 20 | * | * | 4.4 | 100 | * | * | 5.6 |
| As ................................................................................... | 32 | 20 | 94 | 1.3 | 0.8 | 100 | 97 | 0.7 | 1.6 |
| B ..................................................................................... | 210 | 100 | 113 | 2.0 | 1.6 | 400 | 98 | 1.9 | 3.5 |
| Ba ................................................................................... | 39.8 | 20 | 0 | 6.8 | 0.3 | 100 | 0 | 1.6 | 5.7 |
| Be ................................................................................... | 0.32 | 20 | 96 | 0.2 | 0.5 | 100 | 101 | 0.7 | 2.0 |
| Ca ................................................................................... | 48500 | ¥ | ¥ | ¥ | ¥ | ¥ | ¥ | ¥ | ¥ |
| Cd ................................................................................... | 108 | 20 | 98 | 2.5 | 0.8 | 100 | 96 | 0.5 | 0.5 |
| Co ................................................................................... | 5.9 | 20 | 93 | 2.9 | 5.7 | 100 | 93 | 0.6 | 1.5 |
| Cr ................................................................................... | 7580 | 20 | * | * | 0.7 | 100 | * | * | 1.3 |
| Cu ................................................................................... | 806 | 20 | * | * | 1.5 | 100 | 94 | 8.3 | 0.7 |
| Fe ................................................................................... | 31100 | ¥ | ¥ | ¥ | ¥ | ¥ | ¥ | ¥ | ¥ |
| Hg ................................................................................... | 6.1 | 10 | 90 | 2.5 | 4.0 | 40 | 97 | 1.7 | 4.3 |
| K ..................................................................................... | 2390 | 500 | 75 | 8.3 | 4.0 | 2000 | 94 | 2.9 | 3.8 |
| Li .................................................................................... | 9.1 | 10 | 101 | 2.8 | 0.5 | 40 | 106 | 1.6 | 3.1 |
| Mg .................................................................................. | 1950 | 500 | 110 | 2.0 | 0.8 | 2000 | 108 | 2.3 | 3.2 |
| Mn .................................................................................. | 262 | 20 | * | * | 1.8 | 100 | 91 | 1.2 | 0.9 |
| Mo .................................................................................. | 13.2 | 20 | 92 | 2.1 | 2.9 | 100 | 92 | 0.3 | 0.0 |
| Na ................................................................................... | 73400 | 500 | * | * | 1.7 | 2000 | * | * | 1.4 |
| Ni .................................................................................... | 456 | 20 | * | * | 0.4 | 100 | 88 | 2.7 | 0.9 |
| P ..................................................................................... | 9610 | 500 | * | * | 2.9 | 2000 | 114 | 7.4 | 3.4 |
| Pb ................................................................................... | 1420 | 20 | * | * | 2.1 | 100 | * | * | 1.3 |
| Sb ................................................................................... | <2 | 20 | 76 | 0.9 | 3.3 | 100 | 75 | 2.8 | 10.7 |
| Se ................................................................................... | 6.3 | 20 | 86 | 9.0 | 16.6 | 100 | 103 | 1.6 | 2.7 |
| Sn ................................................................................... | 24.0 | 20 | 87 | 4.0 | 2.7 | 80 | 92 | 0.7 | 0.0 |

373

| Sr .................................................................................... | 145 | 100 | 90 | 8.1 | 8.1 | 400 | 93 | 2.4 | 4.6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Tl .................................................................................... | 16 | 20 | 89 | 4.6 | 5.3 | 100 | 92 | 0.8 | 0.9 |
| V ..................................................................................... | 21.7 | 20 | 95 | 1.2 | 1.0 | 100 | 96 | 0.4 | 0.9 |
| Zn ................................................................................... | 12500 | 20 | * | * | 0.8 | 100 | * | * | 0.8 |

Environmental Protection Agency

NBS 1645 River Sediment

| Ag ................................................................................... | 1.6 | 20 | 92 | 0.4 | 1.0 | 100 | 96 | 0.3 | 0.9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Al .................................................................................... | 5160 | 20 | * | * | 8.4 | 100 | * | * | 2.4 |
| As ................................................................................... | 62.8 | 20 | 89 | 14.4 | 9.7 | 100 | 97 | 2.9 | 5.0 |
| B ..................................................................................... | 31.9 | 100 | 116 | 7.1 | 13.5 | 400 | 95 | 0.6 | 1.5 |
| Ba ................................................................................... | 54.8 | 20 | 95 | 6.1 | 2.8 | 100 | 98 | 1.2 | 1.3 |
| Be ................................................................................... | 0.72 | 20 | 101 | 0.4 | 1.0 | 100 | 103 | 1.4 | 3.9 |
| Ca ................................................................................... | 28000 | ¥ | ¥ | ¥ | ¥ | ¥ | ¥ | ¥ | ¥ |
| Cd ................................................................................... | 9.7 | 20 | 100 | 1.1 | 0.0 | 100 | 101 | 0.7 | 1.8 |
| Co ................................................................................... | 9.4 | 20 | 98 | 3.8 | 4.8 | 100 | 98 | 0.9 | 1.8 |
| Cr ................................................................................... | 28500 | 20 | * | * | 0.4 | 100 | * | * | 0.7 |
| Cu ................................................................................... | 109 | 20 | 115 | 8.5 | 0.0 | 100 | 102 | 1.8 | 1.0 |
| Fe ................................................................................... | 84800 | ¥ | ¥ | ¥ | ¥ | ¥ | ¥ | ¥ | ¥ |
| Hg ................................................................................... | 3.1 | 10 | 99 | 4.3 | 7.7 | 40 | 96 | 0.7 | 1.0 |
| K ..................................................................................... | 452 | 500 | 98 | 4.1 | 2.0 | 2000 | 106 | 1.4 | 2.3 |
| Li .................................................................................... | 3.7 | 10 | 101 | 2.0 | 0.7 | 40 | 108 | 1.3 | 3.0 |
| Mg .................................................................................. | 6360 | 500 | * | * | 1.8 | 2000 | 93 | 2.7 | 1.0 |
| Mn .................................................................................. | 728 | 20 | * | * | 3.5 | 100 | 97 | 12.4 | 2.2 |
| Mo .................................................................................. | 17.9 | 20 | 97 | 12.5 | 18.5 | 100 | 98 | 0.6 | 0.0 |
| Na ................................................................................... | 1020 | 500 | 92 | 2.6 | 0.0 | 2000 | 97 | 1.1 | 1.7 |
| Ni .................................................................................... | 36.2 | 20 | 94 | 5.9 | 4.0 | 100 | 100 | 1.1 | 1.5 |
| P ..................................................................................... | 553 | 500 | 102 | 1.4 | 0.9 | 2000 | 100 | 0.8 | 1.6 |
| Pb ................................................................................... | 707 | 20 | * | * | 0.8 | 100 | 103 | 5.9 | 0.4 |
| Sb ................................................................................... | 22.8 | 20 | 86 | 2.3 | 0.0 | 100 | 88 | 0.6 | 0.9 |
| Se ................................................................................... | 6.7 | 20 | 103 | 14.3 | 27.1 | 100 | 98 | 3.1 | 7.6 |
| Sn ................................................................................... | 309 | 20 | * | * | 1.0 | 80 | 101 | 7.9 | 2.7 |
| Sr .................................................................................... | 782 | 100 | 91 | 12.3 | 3.0 | 400 | 96 | 3.3 | 2.6 |
| Tl .................................................................................... | <4 | 20 | 90 | 0.0 | 0.0 | 100 | 95 | 1.3 | 4.0 |
| V ..................................................................................... | 20.1 | 20 | 89 | 5.4 | 5.8 | 100 | 98 | 0.7 | 0.0 |
| Zn ................................................................................... | 1640 | 20 | * | * | 1.8 | 100 | * | * | 1.1 |

Pt. 136, App. C

S (R) Standard deviation of percent recovery.

RPD Relative percent difference between duplicate spike determinations.

<Sample concentration below established method detection limit.

* Spike concentration <10% of sample background concentration.

— Not spiked.

+ Equivalent.

#### Pt. 136, App. C

40 CFR Ch. I (7–1–17 Edition)

TABLE 8—ICP–AES INSTRUMENTAL PRECISION AND ACCURACY FOR AQUEOUS SOLUTIONS A

| Element | Mean conc. (mg/L) | N b | RSD (%) | Accurace c (% of Nominal) |
| --- | --- | --- | --- | --- |
| Al ........................................................................... | 14.8 | 8 | 6.3 | 100 |
| Sb .......................................................................... | 15.1 | 8 | 7.7 | 102 |
| As .......................................................................... | 14.7 | 7 | 6.4 | 99 |
| Ba .......................................................................... | 3.66 | 7 | 3.1 | 99 |
| Be .......................................................................... | 3.78 | 8 | 5.8 | 102 |
| Cd .......................................................................... | 3.61 | 8 | 7.0 | 97 |
| Ca .......................................................................... | 15.0 | 8 | 7.4 | 101 |
| Cr ........................................................................... | 3.75 | 8 | 8.2 | 101 |
| Co .......................................................................... | 3.52 | 8 | 5.9 | 95 |
| Cu .......................................................................... | 3.58 | 8 | 5.6 | 97 |
| Fe .......................................................................... | 14.8 | 8 | 5.9 | 100 |
| Pb .......................................................................... | 14.4 | 7 | 5.9 | 97 |
| Mg ......................................................................... | 14.1 | 8 | 6.5 | 96 |
| Mn ......................................................................... | 3.70 | 8 | 4.3 | 100 |
| Mo ......................................................................... | 3.70 | 8 | 6.9 | 100 |
| Ni ........................................................................... | 3.70 | 7 | 5.7 | 100 |
| K ............................................................................ | 14.1 | 8 | 6.6 | 95 |
| Se .......................................................................... | 15.3 | 8 | 7.5 | 104 |
| Na .......................................................................... | 14.0 | 8 | 4.2 | 95 |
| Tl ........................................................................... | 15.1 | 7 | 8.5 | 102 |
| V ............................................................................ | 3.51 | 8 | 6.6 | 95 |
| Zn .......................................................................... | 3.57 | 8 | 8.3 | 96 |

a These performance values are independent of sample preparation because the labs analyzed portions of the same solutions using sequential or simultaneous instruments.

b N = Number of measurements for mean and relative standard deviation (RSD).

c Accuracy is expressed as a percentage of the nominal value for each analyte in the acidified, multi-element solutions.

TABLE 9—MULTILABORATORY ICP PRECISION AND ACCURACY DATA*

| Analyte | Concentration g/L | Total recoverable digestion /L |
| --- | --- | --- |
| Aluminum ........................................................................................... | 69–4792 | X = 0.9380 (C) + 22.1 |
|  |  | SR = 0.0481 (X) + 18.8 |
| Antimony ............................................................................................ | 77–1406 | 0.8908 (C) + 0.9 |
|  |  | SR = 0.0682 (X) + 2.5 |
| Arsenic ............................................................................................... | 69–1887 | X = 1.0175 (C) + 3.9 |
|  |  | SR = 0.0643 (X) + 10.3 |
| Barium ............................................................................................... | 9–377 | X = 0.8.80 (C) + 1.68 |
|  |  | SR = 0.0826 (X) + 3.54 |
| Beryllium ............................................................................................ | 3–1906 | X = 1.0177 (C) ¥ 0.55 |
|  |  | SR = 0.0445 (X) ¥ 0.10 |
| Boron ................................................................................................. | 19–5189 | X = 0.9676 (C) + 18.7 |
|  |  | SR = 0.0743 (X) + 21.1 |
| Cadmium ........................................................................................... | 9–1943 | X = 1.0137 (C) ¥ 0.65 |
|  |  | SR = 0.0332 (X) + 0.90 |
| Calcium .............................................................................................. | 17–47170 | X = 0.9658 (C) + 0.8 |
|  |  | SR = 0.0327 (X) + 10.1 |
| Chromium .......................................................................................... | 13–1406 | X = 1.0049 (C) ¥ 1.2 |
|  |  | SR = 0.0571 (X) + 1.0 |
| Cobalt ................................................................................................ | 17–2340 | X = 0.9278 (C) + 1.5 |
|  |  | SR = 0.0407 (X) + 0.4 |
| Copper ............................................................................................... | 8–1887 | X = 0.9647 (C) ¥ 3.64 |
|  |  | SR = 0.0406 (X) + 0.96 |
| Iron .................................................................................................... | 13–9359 | X = 0.9830 (C) + 5.7 |
|  |  | SR = 0.0790 (X) + 11.5 |
| Lead ................................................................................................... | 42–4717 | X = 1.0056 (C) + 4.1 |
|  |  | SR = 0.0448 (X) + 3.5 |
| Magnesium ........................................................................................ | 34–13868 | X = 0.9879 (C) + 2.2 |
|  |  | SR = 0.0268 (X) + 8.1 |
| Manganese ........................................................................................ | 4–1887 | X = 0.9725 (C) + 0.07 |
|  |  | SR = 0.0400 (X) + 0.82 |
| Molybdenum ...................................................................................... | 17–1830 | X = 0.9707 (C) ¥ 2.3 |
|  |  | SR = 0.0529 (X) + 2.1 |
| Nickel ................................................................................................. | 17–47170 | X = 0.9869 (C) + 1.5 |
|  |  | SR = 0.0393 (X) + 2.2 |
| Potassium .......................................................................................... | 347–14151 | X = 0.9355 (C) ¥ 183.1 |
|  |  | SR = 0.0329 (X) + 60.9 |
| Selenium ............................................................................................ | 69–1415 | X = 0.9737 (C) ¥ 1.0 |
|  |  | SR = 0.0443 (X) + 6.6 |
| Silicon ................................................................................................ | 189–9434 | X = 0.9737 (C) ¥ 22.6 |

#### Environmental Protection Agency	Pt. 136, App. C

TABLE 9—MULTILABORATORY ICP PRECISION AND ACCURACY DATA*—Continued

| Analyte | Concentration g/L | Total recoverable digestion /L |
| --- | --- | --- |
| Silver .................................................................................................. | 8–189 | SR = 0.2133 (X) + 22.6 |
|  |  | X = 0.3987 (C) + 8.25 |
|  |  | SR = 0.1836 (X) ¥ 0.27 |
| Sodium .............................................................................................. | 35–47170 | X = 1.0526 (C) + 26.7 |
|  |  | SR = 0.0884 (X) + 50.5 |
| Thallium ............................................................................................. | 79–1434 | X = 0.9238 (C) + 5.5 |
|  |  | SR = 0.0106 (X) + 48.0 |
| Vanadium .......................................................................................... | 13–4698 | X = 0.9551 (C) + 0.4 |
|  |  | SR = 0.0472 (X) + 0.5 |
| Zinc .................................................................................................... | 7–7076 | X = 0.9500 (C) + 1.82 |
|  |  | SR = 0.0153 (X) + 7.78 |

*—Regression equations abstracted from Reference 16. X = Mean Recovery, g/L.

C = True Value for the Concentration, g/L. SR = Single-analyst Standard Deviation, g/L.

#### Pt. 136, App. C

40 CFR Ch. I (7–1–17 Edition)

Environmental Protection Agency	§ 140.1

[77 FR 29813, May 18, 2012]

APPENDIX D TO PART 136—PRECISION AND RECOVERY STATEMENTS FOR METHODS FOR MEASURING METALS

Two selected methods from ‘‘Methods for Chemical Analysis of Water and Wastes,’’ EPA–600/4–79–020 (1979) have been subjected to interlaboratory method  validation  stud- ies. The two selected methods are for Thal- lium and Zinc. The following precision and recovery statements are presented in this ap- pendix and incorporated into Part 136:

Method   279.2

For Thallium, Method 279.2 (Atomic Ab- sorption, Furnace Technique) replace the Precision and Accuracy Section statement with the following:

Precision and Accuracy

An interlaboratory study on metal anal- yses by this method was conducted by the Quality Assurance Branch (QAB) of the Envi- ronmental Monitoring Systems Laboratory— Cincinnati (EMSL–CI). Synthetic con- centrates containing various levels of this element were added to reagent water, surface water, drinking water and three effluents. These samples were digested by the total di- gestion procedure, 4.1.3 in this manual. Re- sults for the reagent water are given below. Results for other water types and study de- tails are found in ‘‘EPA Method Study 31, Trace Metals by Atomic Absorption (Fur- nace Techniques),’’ National Technical Infor- mation Service, 5285 Port Royal Road, Springfield, VA 22161 Order No. PB 86–121 704/ AS, by Copeland, F.R. and Maney, J.P., Jan- uary 1986.

For a concentration range of 10.00–252 g/L

X = 0.8781(C) ¥ 0.715  S = 0.1112(X) + 0.669 SR = 0.1005(X) + 0.241

Where:

C = True Value for the Concentration, g/L X = Mean Recovery, g/L

S = Multi-laboratory Standard Deviation, g/

L

SR = Single-analyst Standard Deviation, g/ L

Method   289.2

For Zinc, Method 289.2 (Atomic Absorp- tion, Furnace Technique) replace the Preci- sion and Accuracy Section statement with the following:

Precision and Accuracy

An interlaboratory study on metal anal- yses by this method was conducted by the Quality Assurance Branch (QAB) of the Envi- ronmental Monitoring Systems Laboratory— Cincinnati      (EMSL–CI).      Synthetic      con-

centrates containing various levels of this element were added to reagent water, surface water, drinking water and three effluents. These samples were digested by the total di- gestion procedure, 4.1.3 in this manual. Re- sults for the reagent water are given below. Results for other water types and study de- tails are found in ‘‘EPA Method Study 31, Trace Metals by Atomic Absorption (Fur- nace Techniques),’’ National Technical Infor- mation Service, 5285 Port Royal Road, Springfield, VA 22161 Order No. PB 86–121 704/ AS, by Copeland, F.R. and Maney, J.P., Jan- uary 1986.

For a concentration range of 0.51–189 g/L

X = 1.6710(C) + 1.485 S = 0.6740(X) ¥ 0.342 SR = 0.3895(X)¥ 0.384

Where:

C = True Value for the Concentration, g/L X = Mean Recovery, g/L

S = Multi-laboratory Standard Deviation, g/ L

SR = Single-analyst Standard Deviation, g/ L

[77 FR 29833, May 18, 2012]

# PART 140—MARINE SANITATION DEVICE STANDARD

Sec.

  - Definitions.

  - Scope of standard.

  - Standard.

  - Complete prohibition.

  - Analytical  procedures.   AUTHORITY: 33 U.S.C. 1322, as amended.

SOURCE: 41  FR 4453,  Jan. 29,  1976,  unless

otherwise noted.

##### § 140.1   Definitions.

For the purpose of these standards the following definitions shall apply:

    - Sewage means human body wastes and the wastes from toilets and other receptacles intended to receive or re- tain body wastes;

    - Discharge includes, but is not lim- ited to, any spilling, leaking, pumping, pouring, emitting, emptying, or dump- ing;

    - Marine sanitation device includes any equipment for installation onboard a vessel and which is designed to re- ceive, retain, treat, or discharge sew- age and any process to treat such sew- age;

    - Vessel includes every description of watercraft or other artificial con- trivance used, or capable of being used,

§ 140.2

as a means of transportation on waters of the United States;

    - New vessel refers to any vessel on which construction was initiated on or after January 30, 1975;

    - Existing vessel refers to any  vessel on which construction was initiated be- fore January 30, 1975;

    - Fecal coliform bacteria are those organisms associated with the intes- tines of warm-blooded animals that are commonly used to indicate the pres- ence of fecal material and the potential presence of organisms capable of caus- ing human disease.

##### § 140.2   Scope of standard.

The standard adopted herein applies only to vessels on which a marine sani- tation device has been installed. The standard does not require the installa- tion of a marine sanitation device on any vessel that is not so equipped. The standard applies to vessels owned and operated by the United States unless the Secretary of Defense finds that compliance would not be in the  inter- est of  national  security.

##### § 140.3   Standard.

- (1) In freshwater lakes, freshwater reservoirs or other freshwater im- poundments whose inlets or outlets are such as to prevent the ingress or egress by vessel traffic subject to this regula- tion, or in rivers not capable of naviga- tion by interstate vessel  traffic  subject to this regulation, marine sanitation devices certified by the U.S. Coast Guard (see 33 CFR part 159, published in 40 FR 4622, January 30, 1975), in- stalled on all vessels shall be designed and operated to prevent the overboard discharge of sewage, treated or un- treated, or of any waste derived from sewage. This shall not be construed to prohibit the carriage of Coast Guard- certified flow-through treatment de- vices which have been secured so as to prevent such discharges.

(2) In all other waters, Coast Guard- certified marine sanitation devices in- stalled on all vessels shall be designed and operated to either retain, dispose of, or discharge sewage. If the device has a discharge, subject to paragraph

(d)  of  this  section,  the  effluent  shall not  have  a  fecal  coliform  bacterial count of greater than 1,000 per 100 mil-

#### 40 CFR Ch. I (7–1–17 Edition)

liliters nor visible floating solids. Waters where a Coast Guard-certified marine sanitation device permitting discharge is allowed include coastal waters and estuaries, the Great Lakes and inter-connected waterways, fresh- water lakes and impoundments acces- sible through locks, and other flowing waters that are navigable interstate by vessels subject to this regulation.

- This standard shall become effec- tive on January 30, 1977 for new vessels and on January 30, 1980 for existing vessels (or, in the case of vessels owned and operated by the Department of De- fense, two years and five years, for new and existing vessels, respectively, after promulgation of implementing regula- tions by the Secretary of Defense under section 312(d) of the Act).

- Any vessel which is equipped as of the date of promulgation of this regu- lation with a Coast Guard-certified flow-through marine sanitation device meeting the requirements of paragraph (a)(2) of this section, shall not be re- quired to comply with the provisions designed to prevent the overboard dis- charge of sewage, treated or untreated, in paragraph (a)(1) of this section, for the operable life of that device.

- After January 30, 1980, subject to paragraphs (e) and (f) of this section, marine sanitation devices on all ves- sels on waters that are not subject to a prohibition of  the  overboard  discharge of sewage, treated or untreated, as specified in paragraph (a)(1) of this sec- tion, shall be designed and operated to either retain, dispose of, or discharge sewage,  and  shall  be  certified  by  the

U.S. Coast Guard. If the device has a discharge, the effluent shall not have a fecal coliform bacterial count  of  great- er than 200 per 100 milliliters, nor sus- pended solids greater than 150 mg/1.

- Any existing vessel on waters not subject to a prohibition of the over- board discharge of sewage in paragraph (a)(1) of this section, and which is equipped with a certified device on or before January 30, 1978, shall not be re- quired to comply with paragraph (d) of this section,  for  the  operable  life  of that  device.

- Any new vessel on waters not sub- ject to the prohibition of the overboard discharge of sewage in paragraph (a)(1)

#### Environmental Protection Agency	§ 140.4

of this section, and on which construc- tion is initiated before January 31, 1980, which is equipped with a marine sanitation device before January 31, 1980, certified under paragraph (a)(2) of this section, shall not be required to comply with paragraph (d) of this sec- tion, for the operable life of that de- vice.

- The degrees of treatment de- scribed in paragraphs (a) and (d) of this section are ‘‘appropriate standards’’ for purposes of Coast Guard and Depart- ment of Defense certification  pursuant to section 312(g)(2) of the Act.

[41  FR 4453,  Jan. 29,  1976,  as  amended  at 60

FR 33932, June 29, 1995]

##### § 140.4   Complete prohibition.

- Prohibition pursuant to CWA sec- tion 312(f)(3): a State may completely prohibit the discharge from  all  vessels of any sewage, whether treated or not, into some or all of the waters within such State by making a written appli- cation to the Administrator, Environ- mental Protection Agency, and by re- ceiving  the  Administrator’s  affirma- tive determination pursuant to section 312(f)(3) of the Act. Upon receipt of an application under section 312(f)(3) of the Act, the Administrator will deter- mine within 90 days whether adequate facilities for the safe and sanitary re- moval and treatment of sewage  from all vessels using such waters are rea- sonably available.  Applications  made by States pursuant to section 312(f)(3) of the Act shall include:

  - A certification that the protection and enhancement of the waters de- scribed in the petition require greater environmental protection than the ap- plicable Federal standard;

  - A map showing the location of commercial and recreational pump-out facilities;

  - A description of the location of pump-out facilities within waters des- ignated for no discharge;

  - The general schedule of operating hours of the pump-out facilities;

  - The draught requirements on ves- sels that may be excluded because of insufficient water  depth  adjacent  to the   facility;

  - Information indicating that treat- ment of wastes from such pump-out fa-

cilities  is  in  conformance  with  Federal law; and

  - Information on vessel population and vessel usage of the subject waters.

- Prohibition pursuant to CWA sec- tion 312(f)(4)(A): a State may make a written application to the Adminis- trator, Environmental Protection Agency, under section 312(f)(4)(A) of the Act, for the issuance of a regula- tion completely prohibiting discharge from a vessel of any sewage, whether treated or not, into  particular  waters of the United States or specified por- tions thereof, which waters are located within the boundaries of such State. Such application shall specify with particularly the waters, or portions thereof, for which a complete prohibi- tion is desired. The application shall include identification of water rec- reational areas, drinking  water  in- takes, aquatic sanctuaries, identifiable fish-spawning and nursery areas, and areas of intensive boating activities.  If, on the basis of the State’s application and any other information available to him, the Administrator is unable to make a finding that  the  waters  listed in the application require a complete prohibition of any discharge in the waters or portions thereof covered by the application, he shall state the rea- sons why he cannot make such a find- ing, and shall deny the application.  If the  Administrator  makes  a   finding that the waters listed in the applica- tion require a complete prohibition of any discharge in all or any part of the waters or portions thereof covered by the State’s application, he shall pub- lish notice of such  findings  together with a notice of proposed rule making, and then shall proceed in accordance with 5 U.S.C. 553. If the Administra- tor’s finding is that applicable water quality standards require a complete prohibition covering a more  restricted or more expanded area than that ap- plied for by the State, he  shall  state the reasons why his finding differs in scope from that  requested  in  the State’s   application.

  - For the following waters the dis- charge from a vessel of any sewage (whether treated or not) is completely prohibited pursuant to CWA section 312(f)(4)(A):

#### § 140.4

    - Boundary Waters Canoe Area, for- merly designated as the Superior, Lit- tle Indian Sioux, and Caribou Roadless Areas, in the Superior National Forest, Minnesota, as described in 16 U.S.C. 577–577d1.

    - Waters of the State of Florida within the boundaries of the Florida Keys National Marine Sanctuary as de- lineated on a map of the Sanctuary .(2)(i) For the marine waters of the State of California, the following ves- sels are completely prohibited from discharging any sewage (whether treat- ed or not):

      - A large passenger vessel;

      - A large oceangoing vessel equipped with a holding tank which has not fully used the holding tank’s capacity, or which contains  more  than de minimis amounts of sewage gen- erated while the vessel was outside of the marine waters of the State of Cali- fornia.

- For purposes of paragraph (b)(2) of this section:

  - ‘‘Marine  waters  of  the  State  of California’’   means   the   territorial   sea measured  from  the  baseline  as  deter- mined in  accordance with the  Conven- tion   on   the   Territorial   Sea   and   the Contiguous   Zone   and   extending   sea- ward a distance of three miles, and all enclosed  bays  and  estuaries  subject  to tidal influences from the Oregon border (41.999325 North Latitude, 124.212110 West  Longitude,  decimal  degrees,  NAD 1983) to the Mexican border (32.471231 North  Latitude,  117.137814  West  Lon- gitude,  decimal  degrees,  NAD  1983).  A map  illustrating  these  waters  can  be obtained from EPA or viewed.

  - A ‘‘large  passenger  vessel’’  means a passenger vessel, as defined in section 2101(22) of title 46, United States Code, of 300 gross tons or more, as measured under the International Convention on Tonnage Measurement of Ships, 1969, measurement system in 46 U.S.C. 14302, or the regulatory measurement  system of 46 U.S.C. 14502 for vessels not meas- ured under 46 U.S.C. 14302, that has berths  or  overnight   accommodations for  passengers.

  - A ‘‘large oceangoing vessel’’ means a private, commercial, govern-

#### 40 CFR Ch. I (7–1–17 Edition)

ment, or military vessel of 300 gross tons or more, as measured under the International Convention on Tonnage Measurement of Ships, 1969, measure- ment system in 46 U.S.C. 14302, or the regulatory  measurement  system  of  46

U.S.C. 14502 for vessels not measured under 46 U.S.C.14302, that is not a large passenger vessel.

  - A ‘‘holding tank’’ means a tank specifically designed, constructed, and fitted for the retention of treated or untreated sewage, that has been des- ignated and approved by the ship’s flag Administration on the ship’s stability plan; a designated ballast tank is not a holding tank for this purpose.

(c)(1) Prohibition pursuant to CWA sec- tion 312(f)(4)(B): A State may make written application to the Adminis- trator of the Environmental Protection Agency under section 312(f)(4)(B) of the Act for the issuance of a regulation es- tablishing a drinking water intake no discharge zone which completely pro- hibits discharge from a vessel of any sewage, whether treated or untreated, into that zone in particular waters, or portions thereof, within such State. Such  application  shall:

- Identify and describe exactly and in detail the location of the drinking water supply intake(s) and the commu- nity served by the intake(s), including average and maximum expected amounts of inflow;

- Specify and describe exactly  and in detail, the waters, or portions there- of, for which a complete prohibition is desired, and where appropriate, aver- age, maximum and low flows in million gallons per day (MGD) or the metric equivalent;

- Include a map, either a USGS topographic quadrant map or a NOAA nautical chart, as applicable, clearly marking by latitude and longitude the waters or portions thereof to be des- ignated a drinking water intake zone; and

- Include a statement of basis jus- tifying the size of the requested drink- ing water intake zone, for example, identifying areas of intensive boating activities.

  - If the Administrator finds that a complete prohibition is appropriate under this paragraph, he or she shall publish notice of such finding together

#### Environmental Protection Agency	Pt. 141

with a notice of proposed rulemaking, and then shall proceed in accordance with 5 U.S.C. 553. If the Administra- tor’s finding is that a complete prohibi- tion covering a more restricted or more expanded area than that applied for by the State is appropriate, he or she shall also include a statement of the reasons why the finding differs in scope from that requested in the State’s applica- tion.

  - If the Administrator finds that a complete prohibition is  inappropriate under this paragraph, he or she shall deny the application and state the rea- sons for such denial.

  - For the following waters the dis- charge from a vessel of any sewage, whether treated or not, is completely prohibited pursuant to CWA section 312(f)(4)(B):

    - Two portions of the  Hudson  River in New York State, the  first  is  bounded by an east-west line through the most northern confluence of  the  Mohawk River which will be designated by the Troy-Waterford Bridge (126th Street Bridge) on the south and Lock 2 on the north, and the second of  which  is bounded on the north by the southern end of Houghtaling Island and on the south by a line between the Village of Roseton on the western shore and Low Point on the eastern shore  in  the  vicin- ity of Chelsea, as described in Items  2 and 3 of 6 NYCRR Part 858.4.

    - [Reserved]

[41  FR 4453,  Jan. 29,  1976,  as  amended  at 42

FR 43837,  Aug. 31,  1977;  60  FR 63945,  Dec. 13,

1995; 63 FR 1320, Jan. 8, 1998; 67 FR 35743, May

21, 2002; 77 FR 11411, Feb. 27, 2012]

##### § 140.5   Analytical procedures.

In  determining  the  composition  and quality  of  effluent  discharge  from  ma- rine  sanitation  devices,  the  procedures contained in 40 CFR part 136, ‘‘Guide- lines  Establishing  Test  Procedures  for the  Analysis  of  Pollutants,’’  or  subse- quent  revisions  or  amendments  there- to, shall be employed.

# PART 141—NATIONAL PRIMARY DRINKING WATER REGULATIONS

##### Subpart A—General

Sec.

  - Applicability.

  - Definitions.

  - Coverage.

  - Variances and exemptions.

  - Siting requirements.

  - Effective dates.

##### Subpart B—Maximum Contaminant Levels

  - Maximum contaminant levels for in- organic chemicals.

  - [Reserved]

  - Maximum contaminant levels for tur- bidity.

##### Subpart C—Monitoring and Analytical Requirements

  - Coliform sampling.

  - Turbidity sampling and analytical re- quirements.

  - Inorganic chemical sampling and ana- lytical requirements.

  - Organic chemicals, sampling and ana- lytical requirements.

  - Analytical methods for radioactivity.

  - Monitoring frequency and compliance requirements for radionuclides in com- munity water systems

  - Alternate analytical techniques.

  - Certified laboratories.

  - Monitoring    of    consecutive    public water systems.

APPENDIX A TO SUBPART C OF PART 141—AL- TERNATIVE TESTING METHODS APPROVED FOR ANALYSES UNDER THE SAFE DRINKING WATER ACT

##### Subpart D—Reporting and Recordkeeping

  - Reporting  requirements.

  - [Reserved]

  - Record  maintenance.

  - [Reserved]

  - Reporting  for  unregulated  contami- nant monitoring results.

##### Subpart E—Special Regulations, Including Monitoring Regulations and Prohibition on Lead Use

  - Monitoring requirements for unregu- lated contaminants.

  - Special monitoring for sodium.

  - Special   monitoring   for   corrosivity characteristics.

  - Prohibition on use of lead pipes, sol- der, and flux.

##### Subpart F—Maximum Contaminant Level Goals and Maximum Residual Dis- infectant Level Goals

  - Maximum   contaminant   level   goals for organic contaminants.

  - Maximum   contaminant   level   goals for inorganic contaminants.

Pt. 141

  - Maximum   contaminant   level   goals for microbiological contaminants.

  - Maximum   contaminant   level   goals for disinfection byproducts.

  - Maximum residual disinfectant level goals for disinfectants.

  - Maximum   contaminant   level   goals for radionuclides.

##### Subpart G—National Primary Drinking Water Regulations: Maximum Con- taminant Levels and Maximum Resid- ual Disinfectant Levels

  - Effective dates.

  - Maximum contaminant levels for or- ganic contaminants.

  - Maximum contaminant levels for in- organic contaminants.

  - Maximum contaminant levels (MCLs) for microbiological contaminants.

  - Maximum contaminant levels for dis- infection byproducts.

  - Maximum  residual  disinfectant  lev- els.

  - Maximum    contaminant    levels    for radionuclides.

##### Subpart H—Filtration and Disinfection

  - General requirements.

  - Criteria for avoiding filtration.

  - Disinfection.

  - Filtration.

  - Analytical  and  monitoring  require- ments.

  - Reporting and recordkeeping require- ments.

  - Recycle provisions.

##### Subpart I—Control of Lead and Copper

  - General requirements.

  - Applicability of corrosion control treatment steps to small, medium-size and large water systems.

  - Description    of    corrosion    control treatment requirements.

  - Source    water    treatment    require- ments.

  - Lead   service   line   replacement   re- quirements.

  - Public   education   and   supplemental monitoring  requirements.

  - Monitoring requirements for lead and copper in tap water.

  - Monitoring   requirements   for   water quality  parameters.

  - Monitoring requirements for lead and copper in source water.

  - Analytical methods.

  - Reporting  requirements.

  - Recordkeeping requirements.

#### 40 CFR Ch. I (7–1–17 Edition)

##### Subpart J—Use of Non-Centralized Treatment Devices

  - Criteria and procedures for public water systems using point-of-entry de- vices.

  - Use of bottled water.

##### Subpart K—Treatment Techniques

  - General requirements.

  - Treatment    techniques    for    acryl- amide and epichlorohydrin.

##### Subpart L—Disinfectant Residuals, Disinfec- tion Byproducts, and Disinfection By- product Precursors

  - General requirements.

  - Analytical requirements.

  - Monitoring  requirements.

  - Compliance  requirements.

  - Reporting    and    recordkeeping    re- quirements.

  - Treatment  technique  for  control  of disinfection byproduct (DBP)  precursors.

##### Subparts M–N [Reserved]

Subpart O—Consumer Confidence Reports

  - Purpose   and   applicability   of   this subpart.

  - Effective dates.

  - Content of the reports.

  - Required additional health informa- tion.

  - Report delivery and recordkeeping. APPENDIX A TO SUBPART O OF PART 141—REG-

ULATED  CONTAMINANTS

##### Subpart P—Enhanced Filtration and Dis- infection—Systems Serving 10,000 or More People

  - General requirements.

  - Criteria for avoiding filtration.

  - Disinfection	profiling	and benchmarking.

  - Filtration.

  - Filtration sampling requirements.

  - Reporting    and    recordkeeping    re- quirements.

##### Subpart Q—Public Notification of Drinking Water Violations

  - General public notification require- ments.

  - Tier 1 Public Notice—Form,  manner, and frequency of notice.

  - Tier 2 Public Notice—Form,  manner, and frequency of notice.

  - Tier 3 Public Notice—Form,  manner, and frequency of notice.

  - Content of the public notice.

#### Environmental Protection Agency	Pt. 141

  - Notice to  new billing  units or  new customers.

  - Special notice of the availability of unregulated contaminant monitoring re- sults.

  - Special notice for exceedance of the SMCL for fluoride.

  - Special	notice	for	nitrate exceedances above MCL by  non-commu- nity water systems (NCWS),  where  grant- ed permission by the primacy agency under § 141.11(d).

  - Notice by primacy agency on behalf of the public water system.

  - Special notice for repeated failure to conduct monitoring of the source water for Cryptosporidium and for failure to de- termine bin classification or mean Cryptosporidium level.

APPENDIX A TO SUBPART Q OF PART 141— NPDWR VIOLATIONS AND SITUATIONS RE- QUIRING PUBLIC NOTICE

APPENDIX B TO SUBPART Q OF PART 141— STANDARD  HEALTH   EFFECTS   LANGUAGE FOR PUBLIC NOTIFICATION

APPENDIX C TO SUBPART Q OF PART 141—LIST OF ACRONYMS USED IN PUBLIC NOTIFICA- TION  REGULATION

##### Subpart R [Reserved]

Subpart S—Ground Water Rule

  - General requirements and applica- bility.

  - Sanitary surveys for ground water systems.

  - Ground water source microbial mon- itoring  and  analytical  methods.

  - Treatment technique requirements for ground water systems.

  - Treatment technique violations for ground water systems.

  - Reporting and recordkeeping for ground water systems.

##### Subpart T—Enhanced Filtration and Dis- infection—Systems Serving Fewer Than 10,000 People

GENERAL REQUIREMENTS

141.500   General requirements.

141.501 Who  is  subject  to  the  requirements of subpart T?

141.502 When must my system comply with these   requirements?

141.503 What does subpart T require? FINISHED   WATER   RESERVOIRS

141.510   Is my system subject to the new fin-

ished water reservoir requirements?

141.511 What is required of new  finished water  reservoirs?

ADDITIONAL WATERSHED CONTROL REQUIREMENTS FOR UNFILTERED SYSTEMS

141.520 Is my system subject to the updated watershed  control  requirements?

141.521 What updated  watershed control re- quirements must my unfiltered system implement to continue to  avoid  filtra- tion?

141.522 How does the  State  determine whether my system’s watershed control requirements  are  adequate?

DISINFECTION PROFILE

- What is a disinfection profile and who must develop one?

- What criteria must a State use to determine  that  a  profile  is  unnecessary?

- How does my system develop a dis- infection profile and when must it begin?

- What data must my  system  collect to calculate a disinfection profile?

- How does my system use this data to calculate an inactivation ratio?

- What if my system uses chloramines, ozone, or chlorine dioxide for primary disinfection?

- My system has developed an inac- tivation ratio; what must we do now?

DISINFECTION  BENCHMARK

141.540 Who has to develop a disinfection benchmark?

141.541 What are significant changes to dis- infection    practice?

141.542 What must my system do if we are considering a significant change to dis- infection    practices?

141.543 How is the disinfection benchmark calculated?

141.544  What  if  my  system   uses chloramines, ozone,  or  chlorine  dioxide for  primary  disinfection?

COMBINED FILTER EFFLUENT REQUIREMENTS

141.550 Is  my  system  required to  meet sub- part T combined filter effluent turbidity limits?

141.551 What strengthened combined filter effluent turbidity limits must my system meet?

141.552 My system consists of ‘‘alternative filtration’’ and is required to conduct a demonstration—what is required of my system and how does the State establish my  turbidity  limits?

141.553 My system practices lime soft- ening—is there any special provision re- garding  my  combined  filter  effluent?

INDIVIDUAL FILTER TURBIDITY REQUIREMENTS

141.560 Is my system subject to individual filter   turbidity   requirements?

141.561 What happens if my system’s tur- bidity  monitoring  equipment  fails?

#### Pt. 141

141.562 My system only has two or fewer fil- ters—is there any special provision re- garding individual filter turbidity moni- toring?

141.563 What follow-up action is my system required to take based on continuous turbidity    monitoring?

141.564 My system practices lime soft- ening—is there any special provision re- garding my individual filter turbidity monitoring?

REPORTING  AND  RECORDKEEPING REQUIREMENTS

141.570 What does subpart T require that my system report to the State?

141.571 What records does subpart T require my  system  to  keep?

##### Subpart U—Initial Distribution System Evaluations

141.600   General requirements.

141.601    Standard monitoring. 141.602    System specific studies. 141.603  40/30 certification.

141.604    Very small system waivers.

141.605 Subpart V compliance monitoring location     recommendations.

##### Subpart V—Stage 2 Disinfection Byproducts Requirements

141.620   General requirements.

141.621    Routine monitoring.

141.622    Subpart V monitoring plan. 141.623   Reduced monitoring.

- Additional requirements for con- secutive systems.

- Conditions requiring increased moni- toring.

- Operational evaluation levels.

- Requirements for remaining on re- duced TTHM and HAA5 monitoring based on subpart L results.

- Requirements for remaining on in- creased TTHM and HAA5 monitoring based on subpart L results.

- Reporting and recordkeeping re- quirements.

##### Subpart W—Enhanced Treatment for

Cryptosporidium

GENERAL REQUIREMENTS

141.700   General requirements.

SOURCE WATER MONITORING REQUIREMENTS

141.701    Source water monitoring. 141.702   Sampling schedules.

- Sampling locations.

- Analytical methods.

- Approved laboratories.

- Reporting source water monitoring results.

#### 40 CFR Ch. I (7–1–17 Edition)

- Grandfathering previously collected data.

DISINFECTION  PROFILING  AND  BENCHMARKING REQUIREMENTS

- Requirements when making a sig- nificant change in disinfection practice.

- Developing the disinfection profile and benchmark.

TREATMENT  TECHNIQUE  REQUIREMENTS

- Bin classification  for filtered sys- tems.

- Filtered	system	additional Cryptosporidium   treatment    requirements. 141.712    Unfiltered    system    Cryptosporidium

treatment requirements.

141.713  Schedule	for	compliance	with Cryptosporidium   treatment    requirements. 141.714    Requirements for uncovered finished

water storage facilities.

REQUIREMENTS FOR MICROBIAL TOOLBOX COMPONENTS

- Microbial toolbox options for meet- ing Cryptosporidium treatment require- ments.

- Source toolbox components.

- Pre-filtration treatment toolbox components.

- Treatment performance toolbox components.

- Additional filtration toolbox compo- nents.

- Inactivation toolbox components.

REPORTING  AND  RECORDKEEPING REQUIREMENTS

- Reporting  requirements.

- Recordkeeping requirements.

REQUIREMENTS FOR SANITARY SURVEYS PERFORMED BY EPA

- Requirements to respond to signifi- cant deficiencies identified in sanitary surveys performed by EPA.

##### Subpart X—Aircraft Drinking Water Rule

141.800     Applicability and compliance date. 141.801   Definitions.

141.802    Coliform sampling plan. 141.803    Coliform sampling.

141.804  Aircraft  water   system   operations and  maintenance  plan.

141.805    Notification to passengers and crew. 141.806    Reporting requirements.

141.807    Recordkeeping requirements. 141.808    Audits and inspections.

141.809     Supplemental treatment.

141.810   Violations.

##### Subpart Y—Revised Total Coliform Rule

- General.

#### Environmental Protection Agency	§ 141.2

- Analytical methods and laboratory certification.

- General monitoring requirements for all public water systems.

- Routine monitoring requirements for non-community water systems serv- ing 1,000 or fewer people using only ground water.

- Routine  monitoring   requirements for community water systems serving 1,000 or fewer people using only ground water.

- Routine  monitoring   requirements for subpart H public water systems serv- ing 1,000 or fewer people.

- Routine  monitoring   requirements for public water systems serving more than 1,000 people.

- Repeat monitoring and E. coli re- quirements.

- Coliform treatment technique trig- gers and assessment requirements for protection against potential fecal con- tamination.

- Violations.

- Reporting and recordkeeping.

AUTHORITY: 42 U.S.C. 300f,  300g–1, 300g–2, 300g–3, 300g–4, 300g–5, 300g–6, 300j–4, 300j–9,

and 300j–11.

SOURCE:  40  FR  59570,  Dec.  24,  1975,  unless

otherwise noted.

EDITORIAL NOTE: Nomenclature changes  to part 141 appear at 69 FR 18803, Apr. 9, 2004.

NOTE: For community water systems serv- ing 75,000 or more persons, monitoring must begin 1 year following promulation and the effective date of the MCL is  2 years following promulgation.  For  community  water  sys- tems serving 10,000 to 75,000 persons, moni- toring must begin within 3 years from the date of promulgation and  the  effective  date of the MCL is 4 years from the date of pro- mulgation.   Effective   immediately,   systems that  plan  to   make   significant   modifications to their treatment  processes  for  the  purpose of complying with the TTHM MCL  are  re- quired to seek and obtain State approval of their   treatment   modification   plans.    This note affects §§ 141.2, 141.6, 141.12, 141.24 and

141.30.  For  additional  information  see  44  FR 68641, Nov. 29, 1979.

# Subpart A—General

##### § 141.1   Applicability.

This part  establishes  primary  drink- ing water regulations pursuant to sec- tion 1412 of the Public Health Service Act, as amended by the Safe Drinking Water Act (Pub. L. 93–523); and related regulations applicable to public water systems.

##### § 141.2   Definitions.

As used in this part, the term:

Act means the Public Health Service Act, as amended by the Safe Drinking Water Act, Public Law 93–523.

Action level, is the concentration of lead  or  copper  in  water  specified  in

§ 141.80(c) which determines, in some cases, the treatment requirements con- tained in subpart I of this part that a water  system  is  required  to  complete.

Bag filters are pressure-driven separa- tion devices that remove particulate matter larger than 1 micrometer using an engineered porous filtration media. They are typically constructed of a non-rigid, fabric  filtration  media housed in a pressure vessel in  which the direction of flow is from the inside of the bag to outside.

Bank filtration is a water treatment process that uses a well to recover sur- face water that has naturally infil- trated into ground water through a river bed or bank(s). Infiltration is typically enhanced by the hydraulic gradient imposed by a nearby pumping water supply or other well(s).

Best available technology or BAT means the best technology, treatment techniques, or other means which the Administrator finds, after examination for efficacy under field conditions and not solely under laboratory conditions, are available (taking cost into consid- eration). For the purposes of setting MCLs for synthetic organic chemicals, any BAT must be at least as effective as granular activated carbon.

Cartridge filters are pressure-driven separation devices that remove partic- ulate matter larger than 1 micrometer using an engineered porous filtration media. They are typically  constructed as rigid or semi-rigid, self-supporting filter elements housed in pressure ves- sels in which flow  is  from  the  outside of the cartridge to the inside.

Clean compliance history is, for the purposes of subpart Y, a record of no MCL violations under § 141.63; no moni- toring violations under § 141.21 or sub- part Y; and no coliform treatment technique trigger exceedances or treat- ment technique violations under  sub- part  Y.

Coagulation means a process using co- agulant chemicals and mixing by which colloidal  and  suspended  materials  are

§ 141.2

destabilized   and   agglomerated   into flocs.

Combined distribution system is the interconnected distribution system consisting of the distribution  systems of wholesale systems and of the con- secutive systems that receive finished water.

Community water system means a pub- lic  water  system  which  serves  at  least

15 service connections used by year- round residents or regularly serves at least 25 year-round residents.

Compliance cycle means the nine-year calendar year cycle during which  pub- lic water  systems must  monitor. Each compliance cycle consists of three three-year  compliance   periods.   The first  calendar  year  cycle  begins  Janu- ary 1, 1993 and ends December 31, 2001; the second begins January 1, 2002 and ends December 31, 2010; the third begins January 1, 2011 and ends December 31,

2019.

Compliance period means a three-year calendar year period within a compli- ance cycle. Each compliance cycle has three three-year compliance periods. Within the first compliance cycle, the first compliance period runs from Jan- uary 1, 1993 to December 31, 1995; the second from January 1, 1996 to Decem- ber 31, 1998; the third from January 1,

1999 to December 31, 2001.

Comprehensive performance evaluation (CPE) is a thorough review and anal- ysis of a treatment plant’s perform- ance-based capabilities and associated administrative, operation and mainte- nance practices. It is conducted to identify factors that may be adversely impacting a plant’s capability to achieve compliance and emphasizes ap- proaches that can be implemented without significant capital improve- ments. For purpose of compliance with subparts P and T of this part, the com- prehensive performance evaluation must consist of at least the following components: Assessment of plant per- formance; evaluation of major unit processes;	identification	and prioritization of performance  limiting factors; assessment of the applicability of comprehensive technical assistance; and preparation of a CPE report.

Confluent growth means a continuous bacterial growth covering the entire filtration area of a membrane filter, or

#### 40 CFR Ch. I (7–1–17 Edition)

a portion thereof, in which bacterial colonies are not discrete.

Consecutive system is a public water system that receives some or all of its finished water from one or more whole- sale systems. Delivery may  be through a direct connection or through the dis- tribution system of one or more con- secutive  systems.

Contaminant means any physical, chemical, biological, or radiological substance or matter in water.

Conventional filtration treatment means a series of processes including coagulation, flocculation, sedimenta- tion, and filtration resulting in sub- stantial particulate removal.

Corrosion inhibitor means a substance capable of reducing the corrosivity of water toward metal plumbing mate- rials, especially lead and copper, by forming a protective film on the inte- rior surface of those materials.

CT or CTcalc is the product of ‘‘resid- ual  disinfectant  concentration’’  (C)  in mg/1 determined before or at the first customer, and the corresponding ‘‘dis- infectant contact time’’ (T) in minutes, i.e., ‘‘C’’ ‘‘T’’. If a public water system applies disinfectants at more than one point  prior  to  the  first  customer,  it must  determine  the  CT  of  each  dis- infectant  sequence  before  or  at  the first  customer  to  determine  the  total percent   inactivation   or   ‘‘total   inac- tivation   ratio.’’   In   determining   the total   inactivation   ratio,   the   public water system must determine the re- sidual   disinfectant   concentration   of each  disinfection  sequence  and  cor- responding  contact  time  before  any subsequent	disinfection	application point(s).  ‘‘CT99.9’’  is  the  CT  value  re- quired for 99.9 percent (3–log) inactiva- tion of Giardia lamblia cysts. CT99.9 for a variety of disinfectants and conditions appear in tables 1.1–1.6, 2.1, and 3.1 of

§ 141.74(b)(3).

CTcalc CT99.9

is the inactivation ratio. The sum  of the inactivation ratios, or total inac- tivation ratio shown as

#### Environmental Protection Agency	§ 141.2

(CTcalc)

CT99.9 

is calculated by adding together the in- activation ratio for each disinfection sequence. A total inactivation ratio equal to or greater than 1.0 is assumed to provide a 3-log inactivation of Giardia lamblia cysts.

Diatomaceous earth filtration means a process resulting in substantial partic- ulate removal in which (1) a precoat cake of diatomaceous earth  filter media is deposited on a support membrance (septum), and (2) while the water is filtered by passing through the cake on the septum, additional filter media known as body feed is continu- ously added to the feed water to main- tain  the  permeability  of  the   filter cake.

Direct filtration means a series of processes including coagulation and fil- tration but excluding sedimentation resulting in substantial particulate re- moval.

Disinfectant means any oxidant, in- cluding but not limited to chlorine, chlorine dioxide, chloramines, and ozone added to water in any part of the treatment or distribution process, that is intended to kill or inactivate patho- genic microorganisms.

Disinfectant contact time (‘‘T’’ in CT calculations) means the time in min- utes that it takes for water to move from the point of disinfectant applica- tion or the previous point of disinfect- ant residual measurement to a point before or at the point where residual disinfectant concentration (‘‘C’’) is measured. Where only one ‘‘C’’ is meas- ured, ‘‘T’’ is the time in minutes that it takes for water to move from the point of disinfectant application to a point before or at where residual dis- infectant concentration (‘‘C’’) is meas- ured. Where more than one ‘‘C’’ is measured, ‘‘T’’ is (a) for the first meas- urement of ‘‘C’’, the time in minutes that it takes for water to  move  from the first or only point of disinfectant application to a point before or at the point where the first ‘‘C’’ is measured and (b) for subsequent measurements of ‘‘C’’, the time in minutes that it takes for water to move from the previous ‘‘C’’   measurement   point   to   the   ‘‘C’’

measurement point for which the par- ticular ‘‘T’’ is being calculated. Dis- infectant contact time in pipelines must be  calculated based  on ‘‘plug flow’’ by dividing the internal volume of the pipe by the maximum hourly flow rate through that pipe. Disinfect- ant contact time within mixing basins and storage reservoirs must be deter- mined by tracer studies or an equiva- lent demonstration.

Disinfection means a process which inactivates pathogenic organisms in water by chemical oxidants or equiva- lent  agents.

Disinfection profile is a summary of Giardia lamblia  inactivation  through the treatment plant. The procedure for developing a disinfection profile is con- tained in § 141.172 (Disinfection profiling and benchmarking) in subpart P and §§ 141.530–141.536 (Disinfection profile) in subpart T of this part.

Domestic or other non-distribution sys- tem plumbing problem means a coliform contamination problem in a public water system with more than one serv- ice connection that is limited to the specific service connection from which the coliform-positive sample was taken.

Dose equivalent means the product of the absorbed dose from ionizing radi- ation and such factors as account for differences in biological effectiveness due to the type of radiation and its dis- tribution in the body as specified  by the International Commission on Radi- ological Units  and  Measurements (ICRU).

Dual sample set is a set of two samples collected at the same time and same location, with one sample analyzed for TTHM and the other sample analyzed for HAA5. Dual sample sets are col- lected for the purposes of  conducting an IDSE under subpart U of this  part and determining compliance with the TTHM and HAA5  MCLs  under  subpart V of this part.

Effective corrosion inhibitor residual, for the purpose of subpart I of this part only, means a concentration sufficient to form a passivating film on the inte- rior walls of a pipe.

#### § 141.2

Enhanced coagulation means the addi- tion of sufficient coagulant for im- proved removal of disinfection byprod- uct precursors by conventional filtra- tion treatment.

Enhanced softening means the im- proved removal of disinfection byprod- uct precursors by precipitative soft- ening.

Filter profile is a graphical represen- tation of individual filter performance, based on continuous turbidity meas- urements or total particle counts versus time for an  entire  filter  run, from startup to backwash inclusively, that includes an assessment of filter performance while another filter is being backwashed.

Filtration means a process for remov- ing particulate matter from water by passage through porous media.

Finished water is water that is intro- duced into the distribution system of a public water system and is intended for distribution and consumption without further treatment, except as treatment necessary to maintain water quality in the distribution system (e.g., booster disinfection, addition of corrosion con- trol chemicals).

First draw sample means a one-liter sample of tap water, collected in ac- cordance with § 141.86(b)(2), that has been standing in plumbing  pipes  at least 6 hours and is collected without flushing the tap.

Flocculation means a process to en- hance agglomeration or collection of smaller floc particles into larger, more easily settleable particles through gentle stirring by hydraulic or mechan- ical means.

Flowing stream is a course of running water flowing in a definite channel.

GAC10 means granular activated car- bon filter beds with an empty-bed con- tact time of 10 minutes based on aver- age daily flow and a carbon reactiva- tion frequency of every 180 days, except that the reactivation frequency for GAC10 used as a best available tech- nology for compliance with subpart V MCLs under § 141.64(b)(2) shall be 120 days.

GAC20 means granular activated car- bon filter beds with an empty-bed con- tact time of 20 minutes based on aver- age daily flow and a carbon reactiva- tion frequency of every 240 days.

#### 40 CFR Ch. I (7–1–17 Edition)

Ground water under the direct influence of surface water (GWUDI) means any water beneath the surface  of  the ground with significant occurrence of insects or  other  macroorganisms, algae, or large-diameter  pathogens such as Giardia lamblia or Cryptosporidium, or significant and rel- atively rapid shifts in water character- istics such as turbidity, temperature, conductivity, or pH which closely cor- relate to climatological or  surface water  conditions.  Direct  influence must be determined for individual sources in accordance with criteria es- tablished by the State. The State de- termination of direct influence may be based on site-specific measurements of water quality and/or documentation of well construction characteristics and geology with field evaluation.

Gross alpha particle activity means the total radioactivity due  to  alpha  par- ticle emission as inferred from meas- urements on a dry sample.

Gross beta particle activity means the total radioactivity due to beta particle emission as inferred from measure- ments on a dry sample.

Haloacetic acids (five) (HAA5) mean the sum of the concentrations in milli- grams per liter of the haloacetic acid compounds (monochloroacetic acid, dichloroacetic   acid,   trichloroacetic acid, monobromoacetic acid, and dibro- moacetic acid), rounded to two signifi- cant figures after addition.

Halogen means one of the chemical elements chlorine, bromine or iodine.

Initial compliance period  means  the first full three-year compliance period which begins at least 18 months after promulgation, except for contaminants listed at § 141.61(a) (19)–(21), (c) (19)–(33),

and § 141.62(b) (11)–(15), initial compli- ance period means the first full three- year compliance period after promulga- tion for systems with 150 or more serv- ice connections (January  1993–Decem- ber 1995), and first full three-year com- pliance  period  after  the   effective   date of the regulation (January 1996–Decem- ber 1998) for systems having fewer than 150 service connections.

Lake/reservoir refers to a natural or man made basin or hollow on the Earth’s surface in which water collects or is stored that may or may not have a current or single direction of flow.

#### Environmental Protection Agency	§ 141.2

Large water system, for the purpose of subpart I of this part only, means a water system that serves more than 50,000 persons.

Lead service line means a service line made of lead which connects the water main to the building inlet and any lead pigtail, gooseneck or other  fitting which is connected to such lead line.

Legionella means a genus of bacteria, some species of which have caused a type of pneumonia called Legionnaires Disease.

Level 1 assessment is an evaluation to identify the possible presence of sani- tary defects, defects in distribution system coliform monitoring practices, and (when possible) the likely reason that the system triggered the assess- ment. It is conducted by the system op- erator or owner. Minimum elements in- clude review and identification of atypical events that could affect dis- tributed water quality or indicate that distributed water quality was im- paired; changes in distribution system maintenance and operation that could affect distributed water quality (in- cluding water storage); source and treatment considerations that bear on distributed water quality, where appro- priate (e.g., whether a ground water system is disinfected); existing water quality monitoring data; and inadequa- cies in sample sites, sampling protocol, and sample processing. The system must conduct the assessment con- sistent with any State directives that tailor specific assessment  elements with respect to the size and type of the system and the size, type, and charac- teristics of the distribution system.

Level 2 assessment is an evaluation to identify the possible presence of sani- tary defects, defects in distribution system coliform monitoring practices, and (when possible) the likely reason that the system triggered the assess- ment. A Level 2 assessment provides a more detailed examination of the sys- tem (including the system’s moni- toring and operational practices) than does a Level 1 assessment through the use of more comprehensive investiga- tion and review of available informa- tion, additional internal and external resources, and other relevant practices. It is conducted by an individual ap- proved  by  the  State,  which  may  in-

clude the system operator. Minimum elements include review and identifica- tion of atypical events that could af- fect distributed water quality or indi- cate that distributed water quality was impaired; changes in distribution sys- tem maintenance and operation that could affect distributed water quality (including water storage); source and treatment considerations that bear on distributed water quality, where appro- priate (e.g., whether a ground water system is disinfected); existing water quality monitoring data; and inadequa- cies in sample sites, sampling protocol, and sample processing. The system must conduct the assessment con- sistent with any State directives that tailor specific assessment  elements with respect to the size and type of the system and the size, type, and charac- teristics of the  distribution  system. The system must comply with any ex- pedited actions or additional actions required by the State in the case of an

- coli MCL violation.

Locational running annual average (LRAA) is the average of sample ana- lytical results for samples taken at a particular monitoring location during the previous four calendar quarters.

Man-made beta particle and photon emitters means all radionuclides emit- ting beta particles and/or photons list- ed in Maximum Permissible Body Bur- dens and Maximum Permissible Con- centration of Radionuclides in Air or Water for Occupational Exposure, NBS Handbook 69, except the daughter prod- ucts of thorium–232, uranium–235 and uranium–238.

Maximum contaminant level means the maximum permissable level of a con- taminant in water which is delivered to any user of a public water system.

Maximum contaminant level goal or MCLG means the maximum level of a contaminant in drinking water  at which no known or anticipated adverse effect on the health of persons would occur, and which allows an adequate margin of safety. Maximum contami- nant level goals are nonenforceable health  goals.

Maximum residual disinfectant level (MRDL) means a level of a disinfectant added for water treatment that may not be exceeded at the consumer’s tap without  an  unacceptable  possibility  of

#### § 141.2

adverse health effects. For chlorine and chloramines, a PWS is in compliance with the MRDL when the running an- nual average of monthly averages of samples taken in the distribution sys- tem, computed quarterly, is  less  than or equal to the MRDL. For chlorine di- oxide, a PWS is in compliance with the MRDL when daily samples are taken at the entrance to the distribution system and no two consecutive daily samples exceed the MRDL. MRDLs are enforce- able in  the  same  manner as maximum contaminant levels under Section 1412 of the Safe  Drinking  Water  Act.  There is convincing evidence that addition of a disinfectant is necessary  for  control of waterborne microbial contaminants. Notwithstanding  the  MRDLs   listed  in

§ 141.65, operators may increase resid- ual disinfectant levels of chlorine or chloramines (but not  chlorine  dioxide) in  the  distribution  system  to  a  level and for a time necessary to  protect public health to address specific micro- biological  contamination  problems caused by circumstances such as dis- tribution line  breaks,  storm  runoff events, source water contamination, or cross-connections.

Maximum residual disinfectant level goal (MRDLG) means the maximum level of a disinfectant added for water treatment at which no known or an- ticipated adverse effect on  the  health of persons  would  occur, and  which  al- lows an adequate margin of safety. MRDLGs are nonenforceable health goals and do not reflect the  benefit  of the addition of the chemical for con- trol of waterborne microbial contami- nants.

Maximum Total Trihalomethane Poten- tial (MTP) means the maximum con- centration of total trihalomethanes produced in a given water containing a disinfectant residual after 7 days at a temperature of 25 C or above.

Medium-size water system, for the pur- pose of subpart I of this  part  only, means a water system  that  serves greater than 3,300 and less  than  or equal to 50,000 persons.

Membrane filtration is a pressure or vacuum driven separation process in which particulate matter larger than 1 micrometer is rejected by an engi- neered barrier, primarily through a size-exclusion   mechanism,   and   which

#### 40 CFR Ch. I (7–1–17 Edition)

has a measurable removal efficiency of a target organism that can be verified through the application of a direct in- tegrity test. This definition includes the common membrane technologies of microfiltration, ultrafiltration, nano- filtration, and reverse osmosis.

Near the first service connection means at one of the 20 percent of all service connections in the entire system that are nearest the water supply treatment facility, as measured by water trans- port time within the distribution sys- tem.

Non-community water system means a public water system that is not a com- munity  water  system.  A  non-commu- nity  water  system  is  either  a  ‘‘tran- sient   non-community   water   system (TWS)’’ or a ‘‘non-transient non-com- munity water system (NTNCWS).’’

Non-transient non-community water system or NTNCWS means a public water system that is not a community water system and that regularly serves at least 25 of the same persons over 6 months per year.

Optimal corrosion control treatment, for the purpose of subpart I of this part only, means the corrosion control treatment that minimizes the lead and copper concentrations at users’ taps while insuring that the treatment does not cause the water system to violate any national primary drinking water regulations.

Performance evaluation sample means a reference sample provided to a lab- oratory for the purpose of dem- onstrating that the laboratory can suc- cessfully analyze the sample within limits of performance specified by the Agency. The true value of the con- centration of the reference material is unknown to the laboratory at the time of the analysis.

Person means an individual; corpora- tion; company; association; partner- ship; municipality; or State,  Federal, or tribal agency.

Picocurie (pCi) means the quantity of radioactive material producing 2.22 nu- clear transformations per minute.

Plant intake refers to the works or structures at the head of a conduit through which water is diverted from a source (e.g., river or lake) into the treatment plant.

#### Environmental Protection Agency	§ 141.2

Point of disinfectant application is the point where the disinfectant is applied and water downstream of that point is not subject to recontamination by sur- face water runoff.

Point-of-entry treatment device (POE) is a treatment device applied to the drinking water entering a house or building for the purpose of reducing contaminants in the drinking water distributed throughout the house or building.

Point-of-use treatment device (POU) is a treatment device applied to a single tap used for the purpose of reducing contaminants in drinking water  at that one tap.

Presedimentation is  a  preliminary treatment process used to remove grav- el, sand and other particulate material from the source water through settling before the water enters the primary clarification and  filtration  processes  in a  treatment  plant.

Public water system means a  system for the provision to the public of water for human consumption through pipes or, after August 5, 1998, other con- structed conveyances, if such system has at least fifteen service connections or regularly serves an average of at least twenty-five individuals daily at least 60 days out of the year. Such term includes: any collection, treatment, storage, and distribution  facilities under control of the operator of such system and used primarily in connec- tion with such system; and any collec- tion or pretreatment storage facilities not under such control which are used primarily in connection with such sys- tem. Such term does not include any ‘‘special irrigation district.’’ A public water system is either a ‘‘community water system’’ or a ‘‘noncommunity water  system.’’

Rem means the unit of dose equiva- lent from ionizing radiation  to  the total body or any internal  organ  or organ system. A ‘‘millirem (mrem)’’ is 1⁄1000 of a rem.

Repeat compliance period means any subsequent compliance period after the initial  compliance  period.

Residual  disinfectant  concentration (‘‘C’’ in CT calculations) means the concentration of disinfectant measured in mg/l in a representative sample of water.

Sanitary defect is a defect that could provide a pathway of entry for micro- bial contamination into the distribu- tion system or that is indicative of a failure or imminent failure in a barrier that is already in place.

Sanitary survey means an onsite re- view of the water source, facilities, equipment, operation and maintenance of a public water system for the pur- pose of evaluating the adequacy of such source, facilities, equipment, operation and maintenance for producing and dis- tributing safe drinking water.

Seasonal system is a non-community water system that is not operated as a public water system on a year-round basis and starts up and shuts down at the beginning and end of each oper- ating season.

Sedimentation means a process for re- moval of solids before filtration by gravity or separation.

Service connection, as used in the defi- nition of public water system, does not include a connection to a system that delivers water by a constructed con- veyance other than a pipe if:

  - The water is used exclusively for purposes other than residential uses (consisting of drinking, bathing, and cooking, or other similar uses);

  - The State determines that alter- native water to achieve the equivalent level of public health protection pro- vided by the applicable national pri- mary drinking water regulation is pro- vided for residential or similar uses for drinking and cooking; or

  - The State determines that the water provided for residential or simi- lar uses for drinking, cooking, and bathing is centrally treated or treated at the point of entry by the provider, a pass-through entity, or the user to achieve the equivalent level of protec- tion provided by the applicable na- tional primary drinking water regula- tions.

Service line sample means a one-liter sample  of  water  collected   in   accord- ance with  § 141.86(b)(3),  that  has been standing for at least 6  hours  in  a  serv- ice   line.

Single family structure, for the purpose of subpart I of this part only, means a building constructed as a single-family residence that is currently used as ei- ther a residence or a place of business.

#### § 141.2

Slow sand filtration means a process involving passage of raw water through a bed of sand at low velocity (generally less than 0.4 m/h) resulting in substan- tial particulate removal by physical and biological mechanisms.

Small water system, for the purpose of subpart I of this part only, means a water system that serves 3,300 persons or fewer.

Special irrigation district means an ir- rigation district in  existence  prior  to May 18, 1994 that provides primarily agricultural service through  a  piped water system with only incidental resi- dential or similar use  where  the  system or  the  residential  or  similar  users   of the system comply with the exclusion provisions in section 1401(4)(B)(i)(II) or (III).

Standard sample means the aliquot of finished drinking water that is exam- ined for the presence of coliform bac- teria.

State means the agency of the State or Tribal government which has juris- diction over public water systems. Dur- ing any period when a State or Tribal government does not have primary en- forcement responsibility pursuant to section 1413 of the Act, the term ‘‘State’’ means the Regional Adminis- trator, U.S. Environmental Protection Agency.

Subpart H systems means public water systems using surface water or ground water under the direct influence of sur- face water as a source that are subject to the requirements of subpart H of this  part.

Supplier of water means any person who owns or operates a public water system.

Surface water means all water  which is open to the atmosphere and subject to surface runoff.

SUVA means  Specific  Ultraviolet  Ab- sorption at 254 nanometers (nm), an in- dicator  of  the  humic  content  of  water. It  is  a  calculated  parameter  obtained by  dividing  a  sample’s  ultraviolet  ab- sorption  at  a  wavelength  of  254  nm (UV 254)  (in  m = 1)  by  its  concentra- tion of dissolved organic carbon (DOC) (in mg/L).

System with a single service connection means a system which supplies drink- ing water to consumers via a single service  line.

#### 40 CFR Ch. I (7–1–17 Edition)

Too numerous to count means that the total number of bacterial colonies ex- ceeds 200 on a 47-mm diameter mem- brane filter used for  coliform  detec- tion.

Total Organic Carbon (TOC) means total organic carbon in mg/L measured using heat, oxygen, ultraviolet irradia- tion, chemical oxidants, or combina- tions of these oxidants that convert or- ganic carbon to carbon dioxide, round- ed to two significant figures.

Total trihalomethanes (TTHM) means the sum of the concentration in milli- grams per liter of the trihalomethane compounds (trichloromethane [chloro- form],	dibromochloromethane, bromodichloromethane	and tribromomethane [bromoform]), round- ed to two significant figures.

Transient non-community water system or TWS means a non-community water system that does not regularly serve at least 25 of the same persons over six months per year.

Trihalomethane (THM) means one of the family of organic compounds, named as derivatives of methane, wherein three of the four hydrogen atoms in methane are each substituted by a halogen atom in the molecular structure.

Two-stage lime softening is a process in which chemical addition and hardness precipitation occur in each of two dis- tinct unit clarification processes in se- ries prior to filtration.

Uncovered finished water storage facil- ity is a tank, reservoir, or other facility used to store water that  will  undergo no further treatment to reduce micro- bial pathogens except residual disinfec- tion and is directly open to the atmos- phere.

Virus means a virus of fecal origin which is infectious to humans by wa- terborne transmission.

Waterborne disease outbreak means the significant occurrence of acute infec- tious illness, epidemiologically associ- ated with the ingestion of water from a public water system which is deficient in treatment, as determined by the ap- propriate local or State agency.

Wholesale system is a public water system that treats source water as nec- essary to produce finished water and then delivers some or all of that fin- ished  water  to  another  public  water

#### Environmental Protection Agency	§ 141.6

system. Delivery may be through a di- rect connection or through the dis- tribution system of one or more con- secutive systems.

[40 FR 59570, Dec. 24, 1975]

EDITORIAL NOTE: For FEDERAL REGISTER ci-

tations affecting § 141.2, see the List of CFR Sections Affected, which appears in  the Finding Aids  section of  the printed volume.

##### § 141.3   Coverage.

This part shall apply to each public water system, unless the public water system meets all of the following con- ditions:

- Consists only of distribution and storage facilities (and does not have any collection and treatment facili- ties);

- Obtains all of its water from, but is not owned or operated by, a public water system to which such regula- tions apply:

- Does not sell water to any person; and

- Is not a carrier which conveys passengers in interstate commerce.

##### § 141.4   Variances and exemptions.

- Variances or exemptions from certain provisions of these regulations may be granted pursuant to sections 1415 and 1416 of the Act and subpart K of part 142 of this chapter (for small system variances) by the entity with primary enforcement responsibility, except that variances or exemptions from  the  MCLs  for  total  coliforms  and

E. coli and variances from any of the treatment technique requirements of subpart H of this part may not be granted.

- EPA has stayed the  effective  date of this section relating to the total coliform MCL of § 141.63(a) for systems that demonstrate to the State that the violation of  the  total coliform  MCL  is due to a persistent growth of total coli- forms in the distribution system rather than  fecal  or  pathogenic  contamina- tion,  a  treatment  lapse   or   deficiency, or a problem in the operation or main- tenance  of  the  distribution   system. This is stayed until March 31, 2016, at which  time  the  total  coliform   MCL   is no  longer  effective.

NOTE   TO   PARAGRAPH   (a):  As  provided  in

§ 142.304(a), small system variances are not available for rules addressing microbial con- taminants, which would include subparts H, P, S, T, W, and Y of this part.

[78 FR 10346, Feb. 13, 2013]

##### § 141.5   Siting requirements.

Before a person may enter into a fi- nancial commitment for or initiate construction of a new public water sys- tem or increase the capacity of an ex- isting public water system, he shall no- tify the State and, to the extent prac- ticable, avoid locating part or all of the new or expanded facility at a site which:

    - Is subject to a significant risk from earthquakes, floods, fires or other disasters which could cause a break- down of the public water system or a portion thereof; or

    - Except for intake structures, is within the floodplain of a 100–year flood or is lower than any recorded high tide where appropriate records exist. The U.S. Environmental Protec- tion Agency will not seek to override land use decisions affecting public water systems siting which are made at the  State  or  local government  lev- els.

##### § 141.6   Effective dates.

- Except as provided in paragraphs

- through (k) of this section, and in

§ 141.80(a)(2), the regulations set  forth in  this  part  shall  take   effect   on   June 24, 1977.

  - The regulations for total trihalomethanes set forth in § 141.12(c) shall take effect 2  years  after  the  date of  promulgation   of   these   regulations for community water systems serving 75,000 or more individuals, and 4 years after the date of promulgation for com- munities serving 10,000 to 74,999 indi- viduals.

  - The   regulations   set   forth   in

§§ 141.11(d); 141.21(a), (c) and (i); 141.22(a)

and  (e);  141.23(a)(3)  and  (a)(4);  141.23(f);

141.24(e)    and    (f);    141.25(e);    141.27(a);

141.28(a) and (b); 141.31(a), (d) and (e); 141.32(b)(3); and 141.32(d) shall take ef- fect   immediately   upon   promulgation.

  - The   regulations   set   forth   in

§ 141.41 shall take effect 18 months from the    date    of    promulgation.    Suppliers

#### § 141.11

must complete the first round of sam- pling and reporting within 12 months following the effective date.

  - The   regulations   set   forth   in

§ 141.42 shall take effect 18 months from the date of promulgation. All require- ments in § 141.42 must be completed within 12  months  following  the  effec- tive   date.

  - The   regulations   set   forth   in

§ 141.11(c) and § 141.23(g) are  effective May 2, 1986. Section 141.23(g)(4) is effec- tive October 2, 1987.

  - The   regulations   contained   in

§ 141.6, paragraph (c) of the table in 141.12, and 141.62(b)(1) are effective July 1,   1991.   The   regulations   contained   in

§§ 141.11(b),      141.23,      141.24,      142.57(b),

143.4(b)(12) and (b)(13), are  effective July 30, 1992.  The  regulations  contained in the revisions to §§ 141.32(e) (16), (25) through (27) and (46); 141.61(c)(16); and

141.62(b)(3) are effective January 1, 1993. The effective date of regulations con- tained in § 141.61(c) (2), (3), and (4) is postponed.

  - Regulations     for     the     analytic methods   listed   at   § 141.23(k)(4)   for measuring   antimony,   beryllium,   cya- nide,  nickel,  and  thallium  are  effective August  17,  1992.  Regulations  for  the analytic methods listed at § 141.24(f)(16) for	dichloromethane,	1,2,4- trichlorobenzene,    and    1,1,2-trichloro- ethane  are  effective  August  17,  1992. Regulations   for   the   analytic   methods listed at § 141.24(h)(12) for measuring dalapon,    dinoseb,    diquat,    endothall, endrin,   glyphosate,   oxamyl,   picloram, simazine,		benzo(a)pyrene,	di(2- ethylhexyl)adipate,	di(2- ethylhexyl)phthalate, hexachlorobenzene, hexachlorocyclopentadiene, and 2,3,7,8- TCDD are effective August 17, 1992. The revision to § 141.12(a) promulgated on July 17, 1992 is effective on August 17, 1992.

(i) [Reserved]

- The arsenic maximum  contami- nant levels (MCL) listed in § 141.62 is ef- fective  for  the  purpose  of   compliance on January 23, 2006. Requirements re- lating      to      arsenic      set      forth      in

§§ 141.23(i)(4),  141.23(k)(3)  introductory text, 141.23(k)(3)(ii), 141.51(b), 141.62(b),

141.62(b)(16),    141.62(c),    141.62(d),    and

142.62(b) revisions in Appendix A of sub- part   O   for   the   consumer   confidence

#### 40 CFR Ch. I (7–1–17 Edition)

rule, and Appendices A and B of sub- part Q for the public notification  rule are effective for the purpose of compli- ance on January 23, 2006. However, the consumer confidence rule reporting re- quirements relating to arsenic listed in

§ 141.154(b) and (f) are effective for the purpose of compliance on February 22, 2002.

- Regulations	set	forth	in

§§ 141.23(i)(1),     141.23(i)(2),     141.24(f)(15),

141.24(f)(22),    141.24(h)(11),    141.24(h)(20),

142.16(e), 142.16(j), and 142.16(k) are ef-

fective for the purpose of  compliance on January 22, 2004.

[44 FR 68641, Nov. 29, 1979, as amended at 45

FR 57342, Aug. 27,  1980; 47  FR 10998, Mar. 12,

1982;  51  FR  11410,  Apr.  2,  1986;  56  FR  30274,

July 1, 1991; 57 FR 22178, May 27, 1992; 57 FR

31838, July 17, 1992; 59 FR 34322, July 1, 1994;

61 FR 24368, May 14, 1996; 66 FR 7061, Jan. 22,

2001; 66 FR 28350, May 22, 2001]

# Subpart B—Maximum Contaminant Levels

##### § 141.11   Maximum  contaminant  levels for inorganic chemicals.

- The maximum contaminant  level for arsenic applies only to community water systems. The analyses and deter- mination of compliance with the 0.05 milligrams per liter maximum con- taminant level for arsenic use the re- quirements of § 141.23.

- The maximum contaminant level for arsenic is 0.05 milligrams per  liter for community water systems until January 23, 2006.

- [Reserved]

- At the discretion of the State, ni- trate levels not to exceed 20 mg/l may be allowed in a non-community water system if the supplier of water dem- onstrates to the satisfaction of  the State   that:

  - Such water will not  be  available to children under 6 months of age; and

  - The non-community water  system is meeting the public notification re- quirements under § 141.209, including continuous posting of the fact that ni- trate levels exceed 10 mg/l and the po- tential  health  effects  of  exposure;  and

  - Local and State public health au- thorities will be notified annually of nitrate levels that exceed 10 mg/l; and

Environmental Protection Agency	§ 141.21

  - No adverse health effects shall re- sult.

[40 FR 59570, Dec. 24, 1975, as amended at 45

FR 57342, Aug. 27,  1980; 47  FR 10998, Mar. 12,

1982; 51 FR 11410, Apr. 2, 1986; 56 FR 3578, Jan.

30, 1991; 56 FR 26548, June 7, 1991; 56 FR 30274,

July 1, 1991; 56 FR 32113, July 15, 1991; 60 FR

33932, June 29, 1995; 65 FR 26022, May 4, 2000;

66 FR 7061, Jan. 22, 2001]

##### § 141.12   [Reserved]

§ 141.13   Maximum  contaminant  levels for turbidity.

The  maximum  contaminant   levels for turbidity are applicable to both community water systems and non- community water systems using sur- face water sources in whole or in part. The maximum contaminant levels for turbidity in drinking water,  measured at a representative entry point(s) to the distribution system, are:

    - One turbidity unit (TU), as deter- mined by a monthly  average  pursuant to § 141.22, except that five or fewer tur- bidity units may be allowed if the sup- plier of water can demonstrate to the State  that  the  higher  turbidity  does not do any of the following:

      - Interfere with disinfection;

      - Prevent maintenance of an effec- tive disinfectant agent throughout the distribution system; or

      - Interfere with microbiological de- terminations.

    - Five turbidity units based on an average for two consecutive days pur- suant to § 141.22.

[40 FR 59570, Dec. 24, 1975]

EDITORIAL  NOTE: At 54  FR 27527,  June 29,

1989, § 141.13 was amended by adding intro- ductory text; however, the amendment could not  be  incorporated   because   introductory text   already   exists.

# Subpart C—Monitoring and Analytical Requirements

##### § 141.21   Coliform sampling.

- Routine monitoring. (1) Public water systems must collect total coli- form samples at sites which are rep- resentative of water throughout the distribution system according to a written sample siting plan. These plans are subject to State review and revi- sion.

- The monitoring frequency  for total coliforms for community water systems is based on the population served by the system, as follows:

TOTAL COLIFORM MONITORING FREQUENCY FOR

COMMUNITY WATER SYSTEMS

| Population served | Minimum number of sam- ples per month |
| --- | --- |
| 25 to 1,000 1 .......................................................... | 1 |
| 1,001 to 2,500 ....................................................... | 2 |
| 2,501 to 3,300 ....................................................... | 3 |
| 3,301 to 4,100 ....................................................... | 4 |
| 4,101 to 4,900 ....................................................... | 5 |
| 4,901 to 5,800 ....................................................... | 6 |
| 5,801 to 6,700 ....................................................... | 7 |
| 6,701 to 7,600 ....................................................... | 8 |
| 7,601 to 8,500 ....................................................... | 9 |
| 8,501 to 12,900 ..................................................... | 10 |
| 12,901 to 17,200 ................................................... | 15 |
| 17,201 to 21,500 ................................................... | 20 |
| 21,501 to 25,000 ................................................... | 25 |
| 25,001 to 33,000 ................................................... | 30 |
| 33,001 to 41,000 ................................................... | 40 |
| 41,001 to 50,000 ................................................... | 50 |
| 50,001 to 59,000 ................................................... | 60 |
| 59,001 to 70,000 ................................................... | 70 |
| 70,001 to 83,000 ................................................... | 80 |
| 83,001 to 96,000 ................................................... | 90 |
| 96,001 to 130,000 ................................................. | 100 |
| 130,001 to 220,000 ............................................... | 120 |
| 220,001 to 320,000 ............................................... | 150 |
| 320,001 to 450,000 ............................................... | 180 |
| 450,001 to 600,000 ............................................... | 210 |
| 600,001 to 780,000 ............................................... | 240 |
| 780,001 to 970,000 ............................................... | 270 |
| 970,001 to 1,230,000 ............................................ | 300 |
| 1,230,001 to 1,520,000 ......................................... | 330 |
| 1,520,001 to 1,850,000 ......................................... | 360 |
| 1,850,001 to 2,270,000 ......................................... | 390 |
| 2,270,001 to 3,020,000 ......................................... | 420 |
| 3,020,001 to 3,960,000 ......................................... | 450 |
| 3,960,001 or more ................................................. | 480 |

1 Includes public water systems which have at least 15 service connections, but serve fewer than 25 persons.

If a community water system serving

25 to 1,000 persons has no history of total coliform  contamination  in  its current configuration and a sanitary survey conducted in the past five years shows that the  system  is  supplied  sole- ly by a protected groundwater source and is free of  sanitary  defects,  the State may reduce the monitoring fre- quency specified above, except that  in no case may the State reduce the mon- itoring frequency to less than one  sam- ple per quarter. The State  must  ap- prove the  reduced  monitoring  fre- quency  in  writing.

- The monitoring frequency for total coliforms for non-community water systems is as follows:

§ 141.21

  - A non-community water system using only ground water (except ground water under the direct influ- ence  of  surface  water,  as  defined  in

§ 141.2) and serving 1,000 persons or fewer must monitor each calendar quarter that the system  provides  water to the  public,  except  that  the  State may reduce this monitoring  frequency, in writing, if a sanitary survey shows that the system is free of sanitary de- fects.  Beginning  June  29,  1994,   the State cannot reduce the monitoring frequency for a non-community water system using only  ground  water  (ex- cept ground water under the direct in- fluence  of  surface  water,  as  defined  in

§ 141.2) and serving 1,000 persons or fewer to less than once/year.

  - A non-community water system using only ground water (except ground water under the direct influ- ence  of  surface  water,  as  defined  in

§ 141.2) and serving more than 1,000 per- sons  during  any  month   must   monitor at the same frequency as a like-sized community  water  system,  as   specified in paragraph (a)(2) of this section, ex- cept the State may reduce this moni- toring frequency, in writing, for any month the system serves  1,000  persons or fewer. The State cannot reduce the monitoring frequency to less than once/year. For systems using ground water under the direct influence of sur- face water, paragraph (a)(3)(iv) of this section   applies.

  - A non-community water system using surface water, in total or in part, must monitor at the same frequency as a like-sized community water system, as specified in paragraph (a)(2) of this section, regardless of the number of persons it serves.

  - A non-community water system using ground water under the direct in- fluence of surface water, as defined in

§ 141.2, must monitor at the same fre- quency as a like-sized  community water system, as specified in paragraph (a)(2) of this section. The system must begin monitoring at this frequency be- ginning six months after the State de- termines that the ground water is under the direct influence of surface water.

- The public water system must col- lect samples at regular time intervals throughout  the  month,  except  that  a

#### 40 CFR Ch. I (7–1–17 Edition)

system which uses only ground water (except ground water  under the  direct influence of surface water,  as  defined in § 141.2), and serves 4,900 persons or fewer, may collect all required samples on a single day if they are taken from different  sites.

- A public water system that uses surface water or ground water under the direct influence of surface water, as defined in § 141.2, and does not practice filtration in compliance  with  Subpart H must collect at least one sample near the first service connection each day the turbidity level of the source water, measured as specified in § 141.74(b)(2), exceeds 1 NTU. This sample must be analyzed for the presence of total coli- forms. When one or more turbidity measurements in any day exceed  1 NTU, the system must collect this coli- form sample within 24 hours of the first exceedance, unless the State deter- mines that the system, for logistical reasons outside the system’s control, cannot have the sample analyzed with- in 30 hours of collection. Sample re- sults from this coliform monitoring must be included in determining com- pliance with the MCL for  total  coli- forms in § 141.63.

- Special purpose samples, such as those taken to determine whether dis- infection practices are sufficient fol- lowing pipe placement, replacement, or repair, shall not be used to determine compliance with the MCL for total coliforms in § 141.63. Repeat samples taken pursuant to paragraph (b) of this section are not considered special pur- pose samples, and must be used to de- termine compliance with the MCL for total coliforms in § 141.63.

- Repeat monitoring. (1) If a routine sample is total coliform-positive, the public water system must collect a set of repeat samples within 24 hours of being notified of the positive result. A system which collects more than one routine sample/month must collect no fewer than three repeat samples for each total coliform-positive sample found. A system which collects one routine sample/month or fewer must collect no fewer than four repeat sam- ples for each total coliform-positive sample found. The State may extend the 24-hour limit on a  case-by-case basis   if   the   system   has   a   logistical

#### Environmental Protection Agency	§ 141.21

problem in collecting the repeat sam- ples within 24 hours that is beyond its control. In the case of an  extension, the State must specify how much time the system has to collect the repeat samples.

- The system must collect at least one repeat sample from the sampling tap where the original total coliform- positive sample was taken, and at least one repeat sample at a tap within five service connections upstream and at least one repeat sample at a tap within five service connections downstream of the original sampling site. If a total coliform-positive sample is at the end of the distribution system, or one away from the end of the distribution sys- tem, the State may waive the require- ment to collect at least one repeat sample upstream or downstream of the original sampling site.

- The system must collect all re- peat samples on the same day, except that the State  may  allow  a  system with a single service connection to col- lect the required set of repeat samples over a four-day period or to collect a larger volume repeat sample(s)  in  one or more sample containers of any size, as long as the total volume collected is at least 400 ml (300 ml for systems which collect more than one routine sample/month).

- If one or more repeat samples in the set is total coliform-positive, the public water system must collect an additional set of repeat samples in the manner specified in paragraphs (b) (1)–

- of this section. The additional sam- ples must be collected within 24 hours of being notified of the positive result, unless the State extends the limit as provided in paragraph (b)(1) of this sec- tion. The system must repeat this process until either total coliforms are not detected in one complete set of re- peat samples or the system determines that   the   MCL   for   total   coliforms   in

§ 141.63 has been exceeded and notifies the   State.

(5) If a system collecting fewer than five routine samples/month has one or more total coliform-positive samples and the State does not invalidate the sample(s) under paragraph (c) of this section, it must collect at least five routine samples during the next month the system provides water to the pub-

lic, except that the State may waive this requirement if the conditions of paragraph (b)(5) (i) or (ii) of this sec- tion are met. The State cannot  waive the requirement for a system to collect repeat samples in paragraphs (b) (1)–(4) of this section.

- The State may waive the require- ment to collect five routine samples the next month the system provides water to the public if the State, or an agent approved by the State, performs a site visit before the end of the next month the system provides water to the public. Although a sanitary survey need not be performed, the site visit must be sufficiently detailed to allow the State to determine whether addi- tional monitoring and/or any correc- tive action is needed. The State cannot approve an employee of the system to perform this site visit, even if the em- ployee is an agent approved by the State to perform sanitary surveys.

- The State may waive the require- ment  to  collect  five  routine  samples the next month the system provides water to the public if the State has de- termined why the sample was total coliform-positive  and  establishes   that the system has corrected  the  problem or will correct the problem before the end  of  the  next  month  the  system serves water to the public. In  this  case, the State must document  this  decision to waive the following month’s addi- tional monitoring requirement in writ- ing, have it approved and signed by the supervisor of the State official who recommends such a decision, and make this  document   available   to   the   EPA and public. The written documentation must describe the specific cause of the total   coliform-positive   sample   and what action the system  has  taken  and/ or  will  take  to  correct  this  problem. The State cannot waive the  require- ment  to  collect  five  routine  samples the next month the system provides water to the public  solely  on  the grounds that all repeat  samples  are total coliform-negative. Under this paragraph, a system must still take at least one routine sample before the end of the next month it serves  water  to the public and use it to determine com- pliance with the MCL for  total  coli- forms  in  § 141.63,  unless  the  State  has

#### § 141.21

determined that the system has cor- rected the contamination problem be- fore the system took the set of repeat samples required in paragraphs (b) (1)–

- of this section, and all repeat sam- ples were total coliform-negative.

  - After a system collects a routine sample and before it learns the results of the analysis of that sample, if it col- lects another routine sample(s) from within five adjacent service connec- tions of the initial sample, and the ini- tial sample, after analysis, is found to contain total coliforms, then the sys- tem may count the subsequent sam- ple(s) as a repeat sample instead of as a routine sample.

  - Results of all routine and repeat samples not invalidated by the  State must be included in determining com- pliance with the MCL for  total  coli- forms in § 141.63.

- Invalidation of total coliform sam- ples. A total coliform-positive sample invalidated under this paragraph (c) does not count towards meeting the minimum monitoring requirements of this section.

  - The State may invalidate a total coliform-positive sample only if the conditions of paragraph (c)(1) (i), (ii), or (iii) of this section are met.

    - The laboratory establishes that improper sample analysis caused the total coliform-positive result.

    - The State, on the basis of the re- sults of repeat samples collected as re- quired by paragraphs (b) (1) through (4) of this section, determines that the total coliform-positive sample resulted from a domestic or other non-distribu- tion system plumbing problem. The State cannot invalidate a sample on the basis of repeat sample results un- less all repeat sample(s) collected at the same tap as the original total coli- form-positive sample are also total coliform-positive, and all repeat sam- ples collected within five service con- nections of the original tap are total coliform-negative (e.g., a State cannot invalidate a total coliform-positive sample on the basis of repeat samples if all the repeat samples are total coli- form-negative, or if the public water system has only one service connec- tion).

    - The State has substantial grounds  to  believe  that  a  total  coli-

#### 40 CFR Ch. I (7–1–17 Edition)

form-positive result is due to a cir- cumstance or condition which does not reflect water quality in the distribu- tion system. In this case, the system must still collect all repeat samples re- quired under paragraphs (b) (1)–(4) of this section, and use them to deter- mine compliance with the  MCL  for total coliforms in § 141.63. To invalidate a total coliform-positive sample under this paragraph, the decision with the rationale for the decision must be doc- umented in writing, and approved and signed by the supervisor of the State official who recommended the decision. The State must make this document available to EPA and the public. The written documentation must state the specific cause of the total coliform- positive sample, and what action the system has taken, or will take, to cor- rect this problem. The State may not invalidate a total coliform-positive sample solely on the grounds that all repeat samples are total coliform-nega- tive.

  - A laboratory must invalidate a total coliform sample (unless total coliforms are detected) if the sample produces a turbid culture in the ab- sence of gas production using an ana- lytical method where gas formation is examined (e.g., the Multiple-Tube Fer- mentation Technique), produces  a turbid culture in the absence of an acid reaction in the Presence-Absence (P-A) Coliform Test, or exhibits confluent growth or produces colonies too numer- ous to count with an analytical method using a membrane filter (e.g., Mem- brane Filter Technique).  If  a  labora- tory invalidates a sample because of such interference, the system must col- lect another  sample from the  same lo- cation as the original sample within 24 hours of being notified of the inter- ference problem, and have it analyzed for the presence of total coliforms. The system must continue to re-sample within 24 hours and have the samples analyzed until it obtains a valid result. The State may waive the 24-hour time limit on a case-by-case basis.

- Sanitary surveys. (1)(i) Public water systems which do not collect five or more routine samples/month must undergo an initial sanitary survey by June 29, 1994, for community public water  systems  and  June  29,  1999,  for

#### Environmental Protection Agency	§ 141.21

non-community water systems. There- after, systems must undergo another sanitary survey every five years, ex- cept that non-community water sys- tems using only protected and dis- infected ground water, as defined by the State, must undergo subsequent sanitary surveys at  least every ten years after the initial sanitary survey. The State must review the results of each sanitary survey to determine whether the existing monitoring fre- quency is adequate and what additional measures, if any, the system needs to undertake to improve drinking water quality.

(ii) In conducting a  sanitary  survey of a system using ground water in a State having an EPA-approved well- head protection program under section 1428 of the Safe Drinking Water Act, information on sources of contamina- tion within the delineated wellhead protection area that was collected in the course of developing and imple- menting the program should be consid- ered instead of collecting new informa- tion, if the information was collected since the last time the system was sub- ject to a sanitary survey.

- Sanitary surveys must be per- formed by the State or an agent ap- proved by the State. The system is re- sponsible for ensuring the survey takes place.

- Sanitary surveys conducted  by the    State    under    the    provisions    of

§ 142.16(o)(2) of this chapter  may  be used to meet the sanitary survey re- quirements  of  this  section.

- Fecal coliforms/Escherichia coli (E. coli) testing. (1) If any routine or repeat sample is total coliform-positive, the system must analyze that total coli- form-positive culture medium to deter- mine if fecal coliforms are present, ex- cept that the system may test for  E. coli in lieu of fecal coliforms. If fecal coliforms or E. coli are present, the sys- tem must notify the State by the end of the day when the system is notified of the test result, unless the system is notified of the result after the State of- fice is closed, in which case the system must notify the State before the end of the next business day.

(2) The State has the discretion to allow a public water system, on a case- by-case basis, to forgo fecal coliform or

E. coli testing on a total coliform-posi- tive sample if  that  system  assumes that the total  coliform-positive  sample is fecal coliform-positive or E. coli-posi- tive. Accordingly, the system must no- tify the State as specified in paragraph (e)(1) of this section and the provisions of § 141.63(b) apply.

- Analytical methodology. (1) The standard sample volume required for total coliform analysis, regardless of analytical method used, is 100 ml.

- Public water systems need only determine the presence or absence of total coliforms; a determination of total coliform density is not required.

- Public water systems must con- duct total coliform analyses in accord- ance with one of the analytical meth- ods in the following table or one of the alternative methods listed in appendix A to subpart C of this part.

| Organism | Methodology 12 | Citation 1 |
| --- | --- | --- |
| Total Coliforms 2 .............. | Total Coliform Fermentation Technique 3 4 5 ................................................... | 9221A, B. |
|  | Total Coliform Membrane Filter Technique 6 ................................................... | 9222A, B, C. |
|  | Presence-Absence (P-A) Coliform Test 5 7 ...................................................... | 9221D. |
|  | ONPG-MUG Test 8 .......................................................................................... | 9223. |
|  | Colisure Test. 9 |  |
|  | E*Colite Test. 10 |  |
|  | m-ColiBlue24 Test. 11 |  |
|  | Readycult Coliforms 100 Presence/Absence Test. 13 |  |
|  | Membrane Filter Technique using Chromocult Coliform Agar. 14 |  |
|  | Colitag Test. 15 |  |

The procedures shall be done in accordance with the documents listed below. The incorporation by reference of the following documents listed in footnotes 1, 6, 8, 9, 10 , 11, 13, 14 and 15 was approved by the Director of the Federal Register in accord- ance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies of the documents may be obtained from the sources listed below. Informa- tion regarding obtaining these documents can be obtained from the Safe Drinking Water Hotline at 800–426–4791. Documents may be inspected at EPA’s Drinking Water Docket, EPA West, 1301 Constitution Avenue, NW., EPA West, Room B102, Wash- ington DC 20460 (Telephone: 202–566–2426); or at the National Archives and Records Administration (NARA). For information on the availability of this material at NARA, call 202–741–6030

#### § 141.21

40 CFR Ch. I (7–1–17 Edition)

1 Standard Methods for the Examination of Water and Wastewater, 18th edition (1992), 19th edition (1995), or 20th edition (1998). American Public Health Association, 1015 Fifteenth Street, NW., Washington, DC 20005. The cited methods published in any of these three editions may be used. In addition, the following online versions may also be used: 9221 A, B, D–99, 9222 A, B, C–97, and 9223 B–97. Standard Methods Online are available The year in which each method was approved by the Standard Methods Committee is designated by the last two digits in the method number. The methods listed are the only Online versions that may be used.

2 The time from sample collection to initiation of analysis may not exceed 30 hours. Systems are encouraged but not required to hold samples below 10 deg. C during transit.

3 Lactose broth, as commercially available, may be used in lieu of lauryl tryptose broth, if the system conducts at least 25 par- allel tests between this medium and lauryl tryptose broth using the water normally tested, and this comparison demonstrates that the false-positive rate and false-negative rate for total coliform, using lactose broth, is less than 10 percent.

4 If inverted tubes are used to detect gas production, the media should cover these tubes at least one-half to two-thirds after the sample is added.

5 No requirement exists to run the completed phase on 10 percent of all total coliform-positive confirmed tubes.

6 MI agar also may be used. Preparation and use of MI agar is set forth in the article, ‘‘New medium for the simultaneous de- tection of total coliform and Escherichia coli in water’’ by Brenner, K.P., et. al., 1993, Appl. Environ. Microbiol. 59:3534–3544. Also available from the Office of Water Resource Center (RC–4100T), 1200 Pennsylvania Avenue, NW., Washington, DC 20460, EPA/600/J–99/225. Verification of colonies is not required.

7 Six-times formulation strength may be used if the medium is filter-sterilized rather than autoclaved.

8 The ONPG-MUG Test is also known as the Autoanalysis Collect System.

9 A description of the Colisure Test, Feb 28, 1994, may be obtained from IDEXX Laboratories, Inc., One IDEXX  Drive, Westbrook, Maine 04092. The Colisure Test may be read after an incubation time of 24 hours.

10 A description of the E*Colite Test, ‘‘Presence/Absence for Coliforms and E. Coli in Water,’’ Dec 21, 1997, is available from Charm Sciences, Inc., 36 Franklin Street, Malden, MA 02148–4120.

11 A description of the m-ColiBlue24 Test, Aug 17, 1999, is available from the Hach Company, 100 Dayton Avenue, Ames, IA 50010.

12 EPA strongly recommends that laboratories evaluate the false-positive and negative rates for the method(s) they use for monitoring total coliforms. EPA also encourages laboratories to establish false-positive and false-negative rates within their own laboratory and sample matrix (drinking water or source water) with the intent that if the method they choose has an unacceptable false-positive or negative rate, another method can be used. The Agency suggests that laboratories perform these studies on a minimum of 5% of all total coliform-positive samples, except for those methods where verification/confirmation is already re- quired, e.g., the M-Endo and LES Endo Membrane Filter Tests, Standard Total Coliform Fermentation Technique, and Presence- Absence Coliform Test. Methods for establishing false-positive and negative-rates may be based on lactose fermentation, the rapid test for b-galactosidase and cytochrome oxidase, multi-test identification systems, or equivalent confirmation tests. False- positive and false-negative information is often available in published studies and/or from the manufacturer(s).

13 The Readycult Coliforms 100 Presence/Absence Test is described in the document, ‘‘Readycult Coliforms 100 Presence/ Absence Test for Detection and Identification of Coliform Bacteria and Escherichla coli in Finished Waters’’,  November 2000, Version 1.0, available from EM Science (an affiliate of Merck KGgA, Darmstadt Germany), 480 S. Democrat Road, Gibbstown, NJ 08027–1297. Telephone number is (800) 222–0342, e-mail address is: adellenbusch@emscience.com.

14 Membrane Filter Technique using Chromocult Coliform Agar is described in the document, ‘‘Chromocult    Coliform Agar Presence/Absence Membrane Filter Test Method for Detection and Identification of Coliform Bacteria and Escherichla coli in Fin- ished Waters’’, November 2000, Version 1.0, available from EM Science (an affiliate of Merck KGgA, Darmstadt Germany), 480

S.    Democrat    Road,    Gibbstown,    NJ    08027–1297.    Telephone    number    is    (800)    222–0342,    e-mail    address    is:

adellenbusch@emscience.com.

15 Colitag product for the determination of the presence/absence of total coliforms and E. coli is described in ‘‘Colitag Prod- uct as a Test for Detection and Identification of Coliforms and E. coli Bacteria in Drinking Water and Source Water as Required in National Primary Drinking Water Regulations,’’ August 2001, available from CPI International, Inc., 5580 Skylane Blvd., Santa Rosa, CA, 95403, telephone (800) 878–7654, Fax (707) 545–7901

- [Reserved]

- Public water systems must con- duct fecal coliform analysis in accord- ance with the following procedure. When the MTF Technique or Presence- Absence (PA) Coliform Test is used to test for total coliforms, shake the lac- tose-positive presumptive tube or P-A vigorously and transfer the growth with a sterile 3-mm loop or sterile ap- plicator stick into brilliant green lac- tose bile broth and EC medium to de- termine the presence of total and fecal coliforms, respectively. For EPA-ap- proved analytical methods which use a membrane filter, transfer the total coliform-positive culture by one of the following methods: remove the mem- brane containing the total coliform colonies from the substrate with a ster- ile forceps and carefully curl and insert the membrane into a tube of EC me- dium (the laboratory may first remove a small portion of selected colonies for verification),  swab  the  entire  mem-

brane filter surface with a sterile cot- ton swab and transfer the inoculum to EC medium (do not leave the cotton swab in the EC medium), or inoculate individual total coliform-positive colo- nies into EC Medium. Gently shake the inoculated tubes of EC medium to in- sure adequate mixing and incubate in a waterbath at 44.5 0.2 C for 24 2 hours. Gas production of any amount in the inner fermentation tube of the EC me- dium indicates a positive fecal coliform test. The preparation of EC medium is described in Method 9221E (paragraph 1a) in Standard Methods for the Exam- ination of Water and Wastewater, 18th edition (1992), 19th edition (1995), and 20th edition (1998); the cited method in any one of these three editions may be used. Public water systems need only determine the presence or absence of fecal  coliforms;  a  determination  of fecal coliform density is not required.

#### Environmental Protection Agency	§ 141.21

- Public water systems must con- duct analysis of Escherichia coli in ac- cordance with one of the following ana- lytical methods or one of the alter- native methods listed in appendix A to subpart C of this part.

  - EC  medium  supplemented  with  50

g/mL of 4-methylumbelliferyl-beta-D- glucuronide (MUG)  (final  concentra- tion), as described in Method 9222G in Standard Methods for the  Examination of Water and Wastewater, 19th edition (1995) and 20th edition (1998). Either edition may be used. Alternatively, the 18th edition (1992) may be used if at least 10 mL of EC medium, as described in paragraph (f)(5) of this section, is supplemented with 50 g/mL of MUG before autoclaving. The inner inverted fermentation  tube  may  be  omitted.  If the 18th edition is used, apply the pro- cedure in paragraph (f)(5) of this sec- tion for transferring a total coliform- positive culture to EC medium supple- mented  with  MUG,  incubate   the   tube at 44.5 0.2 C for 24 2 hours, and then observe fluorescence with  an  ultra- violet light  (366  nm) in  the  dark. If  flu- orescence  is  visible,  E.  coli  are  present.

  - Nutrient  agar  supplemented  with

100 g/mL of 4-methylumbelliferyl- beta-D-glucuronide (MUG) (final con- centration), as described in Method 9222G in Standard Methods for the Ex- amination of Water and Wastewater, 19th edition (1995) and 20th edition (1998). Either edition may be used for determining if a total coliform-positive sample, as determined by a membrane filter technique, contains E. coli. Al- ternatively, the 18th edition (1992) may be used if the membrane filter con- taining a total coliform-positive col- ony(ies) is transferred to nutrient agar, as described in Method 9221B (para- graph 3) of Standard Methods (18th edi- tion), supplemented with 100 g/mL of MUG. If the 18th edition is used, incu- bate the agar plate at 35 C for 4 hours and then observe the colony(ies) under ultraviolet light (366 nm) in the  dark for fluorescence. If fluorescence is visi- ble, E. coli are present.

  - Minimal Medium ONPG-MUG (MMO-MUG) Test, as set forth in the article ‘‘National Field Evaluation of a Defined Substrate Method for the Si- multaneous Detection of Total Coli- forms and Escherichia coli from Drink-

ing Water: Comparison with Presence- Absence Techniques’’ (Edberg et al.), Applied and Environmental Microbi- ology, Volume 55, pp. 1003–1008, April 1989. (Note: The Autoanalysis Colilert System is an MMO-MUG test). If the MMO-MUG test is  total  coliform-posi- tive after a 24-hour incubation, test the medium for fluorescence with  a 366-nm ultraviolet light (preferably with  a  6- watt lamp) in  the  dark.  If  fluorescence is observed, the sample is E. coli-posi- tive. If fluorescence is questionable (cannot be definitively read) after 24 hours incubation,  incubate  the  culture for an additional four hours (but not to exceed 28 hours total), and again  test the medium for fluorescence. The MMO-MUG Test  with  hepes  buffer  in lieu of phosphate buffer is the only ap- proved  formulation  for  the  detection  of

E. coli.

  - The Colisure Test. A  description of the Colisure Test may be obtained  from the Millipore Corporation, Technical Services Department, 80 Ashby Road, Bedford, MA 01730.

  - The membrane filter method with MI agar, a description  of  which  is  cited in footnote 6 to the table in paragraph (f)(3) of this section.

  - E*Colite Test,   a  description of which is  cited  in   footnote 10 to the table at paragraph  (f)(3) of this section.

  - m-ColiBlue24 Test, a   descrip- tion of which is cited in  footnote 11 to the table in paragraph  (f)(3) of this sec- tion.

  - Readycult Coliforms 100  Pres- ence/Absence   Test,   a    description of which is cited  in   footnote 13 to the table at paragraph  (f)(3) of this section.

  - Membrane Filter Technique using  Chromocult Coliform   Agar, a description of which is cited   in foot- note 14 to the table at  paragraph (f)(3) of this section.

  - Colitag , a description of  which is cited in footnote 15 to the   table  at paragraph (f)(3) of this  section.

- As an option to paragraph (f)(6)(iii) of this section, a system with a total coliform-positive, MUG-nega- tive, MMO-MUG test may further ana- lyze the culture for the presence of E. coli by transferring a 0.1 ml, 28-hour MMO-MUG culture to EC Medium + MUG with a pipet. The formulation and incubation conditions of EC Medium +

#### § 141.22

MUG, and  observation  of  the  results are described in paragraph (f)(6)(i) of this  section.

- The following materials are incor- porated by reference in  this  section with the approval of the Director of the Federal  Register  in  accordance  with  5

U.S.C. 552(a) and 1 CFR part 51. Copies of  the  analytical  methods  cited  in Standard Methods for the Examination of Water and Wastewater (18th, 19th, and  20th  editions)  may  be  obtained from the American Public Health Asso- ciation  et  al.;  1015  Fifteenth  Street, NW., Washington, DC 20005–2605. Copies of the MMO-MUG Test, as set forth in the article ‘‘National Field Evaluation of a Defined Substrate Method for the Simultaneous  Enumeration  of  Total Coliforms  and  Escherichia  coli  from Drinking Water: Comparison with the Standard Multiple Tube Fermentation Method’’  (Edberg  et al.)  may  be  ob- tained from the American Water Works Association Research Foundation, 6666 West Quincy Avenue, Denver, CO 80235. Copies of the MMO-MUG Test as set forth  in  the  article  ‘‘National  Field Evaluation   of   a   Defined   Substrate Method  for  the  Simultaneous  Enu- meration of Total Coliforms and Esch- erichia coli from Drinking Water: Com- parison  with  the  Standard  Multiple Tube Fermentation Method’’ (Edberg et al.) may be obtained from the Amer- ican  Water  Works  Association  Re- search Foundation, 6666 West Quincy Avenue, Denver, CO 80235. A descrip- tion of the Colisure Test may be  ob- tained from the Millipore Corp., Tech- nical Services Department, 80 Ashby Road, Bedford, MA 01730. Copies may be inspected  at  EPA’s  Drinking  Water Docket; 401  M St., SW.; Washington, DC 20460, or at the National Archives and Records Administration (NARA). For information on the availability of this material at NARA, call 202–741– 6030.

- Response to violation. (1) A public water system which has exceeded the MCL for total coliforms in § 141.63 must report the violation to the State no later than the end of the next business day after it learns of the violation, and

#### 40 CFR Ch. I (7–1–17 Edition)

notify the public in accordance with subpart Q.

(2) A public water system which has failed to comply with a coliform moni- toring requirement,  including  the  sani- tary survey requirement, must report the monitoring violation to the State within ten days after the system dis- covers the violation, and notify the public in accordance with subpart Q.

- The provisions of paragraphs (a) and (d) of this section are applicable until March 31, 2016. The provisions of paragraphs (b), (c), (e), (f), and (g)  of this section are applicable until all re- quired repeat monitoring under para- graph (b) of this section and fecal coli- form or E. coli testing under paragraph

- of this section that was initiated by a total coliform-positive sample taken before April 1, 2016 is completed, as well as analytical method, reporting, recordkeeping, public notification, and consumer confidence report require- ments associated with that monitoring and testing. Beginning April 1, 2016, the provisions of subpart Y of this part are applicable, with systems required to begin regular monitoring at the same frequency as the system-specific fre- quency required on March 31, 2016.

[54 FR 27562, June 29, 1989]

EDITORIAL NOTE: For FEDERAL REGISTER ci-

tations affecting § 141.21, see the List of CFR Sections Affected, which appears in  the Finding Aids  section of  the printed volume

##### § 141.22   Turbidity  sampling  and  ana- lytical requirements.

The requirements in  this  section apply to unfiltered systems until De- cember 30, 1991, unless the State has determined prior to that date, in  writ- ing pursuant to section 1412(b)(7)(iii), that filtration is required. The require- ments in this section apply to filtered systems until June 29, 1993. The re- quirements in this section apply to unfiltered systems that the State has determined, in writing pursuant to sec- tion 1412(b)(7)(C)(iii), must install fil- tration, until June 29, 1993, or until fil- tration  is  installed,  whichever  is  later.

  - Samples shall be taken by sup- pliers of water for both community and non-community water  systems at  a representative entry point(s) to the water distribution system at least once

#### Environmental Protection Agency	§ 141.23

per day, for the purposes of making turbidity measurements to determine compliance with § 141.13. If the State determines that a reduced sampling frequency in a non-community will not pose a risk to public health, it can re- duce the required sampling frequency. The option of reducing the turbidity frequency shall be permitted only in those public water systems that prac- tice  disinfection  and  which  maintain an active residual disinfectant in the distribution system, and in those cases where the State has indicated in writ- ing that no unreasonable risk to health existed under the circumstances of this option. Turbidity measurements shall be made as directed in § 141.74(a)(1).

  - If the result of a turbidity anal- ysis indicates that the maximum al- lowable limit has been exceeded, the sampling and measurement shall be confirmed by resampling as soon as practicable and preferably within one hour. If the  repeat  sample  confirms that the maximum allowable limit has been exceeded, the supplier  of  water shall report to the State within  48 hours. The repeat sample shall be the sample used for the purpose of calcu- lating the monthly average. If the monthly average of the daily samples exceeds  the  maximum  allowable   limit, or if the average of  two  samples  taken on consecutive days exceeds 5 TU, the supplier of water shall  report  to  the State and notify the  public  as  directed in § 141.31 and subpart Q.

  - Sampling for non-community water systems shall begin within two years after the effective date of this part.

  - The requirements of this § 141.22 shall apply only to  public  water  sys- tems which  use  water  obtained  in whole  or  in  part  from  surface  sources.

  - The State has the authority to de- termine compliance or initiate enforce- ment action based upon analytical re- sults or other information compiled by their sanctioned representatives and agencies.

[40 FR 59570, Dec. 24, 1975, as amended at 45

FR  57344,  Aug.  27,  1980;  47  FR  8998,  Mar.  3,

1982; 47 FR 10998, Mar. 12, 1982; 54 FR 27527,

June 29, 1989; 59 FR 62466, Dec. 5, 1994; 65 FR

26022, May 4, 2000]

##### § 141.23   Inorganic  chemical  sampling and analytical requirements.

Community water systems shall con- duct monitoring to determine compli- ance with the maximum contaminant levels specified in § 141.62 in accordance with this section. Non-transient, non- community water systems shall con- duct monitoring to determine compli- ance with the maximum contaminant levels specified in § 141.62 in accordance with this section. Transient, non-com- munity water systems shall conduct monitoring to determine  compliance with the nitrate and  nitrite maximum contaminant    levels    in    §§ 141.11    and

  - (as   appropriate)   in   accordance with this section.

    - Monitoring shall be conducted as follows:

      - Groundwater systems shall take a minimum of one sample at every entry point to the distribution system which is representative of each well after treatment (hereafter called a sampling point) beginning in the initial compli- ance period. The system  shall  take each sample at the same  sampling point unless conditions make another sampling point more representative of each source or treatment plant.

      - Surface water  systems  shall  take a minimum of one  sample  at  every entry point to the distribution system after any application of  treatment  or in the distribution system at a point which is representative of each source after treatment (hereafter called a sampling point) beginning in the ini- tial compliance period. The system shall take each sample at the same sampling point unless conditions make another sampling point more rep- resentative of each source or treatment plant.

NOTE: For purposes of this paragraph, sur- face water systems include systems with a combination of surface and ground sources.

      - If a system draws water from more than one source and the sources are combined before distribution, the system must sample at  an  entry  point to the distribution system during peri- ods of normal operating  conditions (i.e., when water is representative of all sources being used).

#### § 141.23

      - The State may reduce the total number of samples which must be ana- lyzed by allowing the use of compositing. Composite samples from a maximum of five samples are al- lowed, provided that the detection limit of the method used for analysis is less than one-fifth of the MCL. Compositing of samples must be done in the laboratory.

        - If the concentration in the com- posite sample is greater than or equal

#### 40 CFR Ch. I (7–1–17 Edition)

to one-fifth of the MCL of any inor- ganic chemical, then a follow-up sam- ple must be taken within 14 days at each sampling point included in the composite. These samples must be ana- lyzed for the contaminants which ex- ceeded one-fifth of the MCL in the composite sample. Detection limits for each analytical method and MCLs for each inorganic contaminant are the following:

DETECTION LIMITS FOR INORGANIC CONTAMINANTS

| Contaminant | MCL (mg/l) | Methodology | Detection limit (mg/l) |
| --- | --- | --- | --- |
| Antimony ............................. | 0.006 ........ | Atomic Absorption; Furnace ............................................................... | 0.003 |
|  |  | Atomic Absorption; Platform .............................................................. | 0.0008 5 |
|  |  | ICP-Mass Spectrometry ..................................................................... | 0.0004 |
|  |  | Hydride-Atomic Absorption ................................................................ | 0.001 |
| Arsenic ................................ | 0.010 6 ..... | Atomic Absorption; Furnace ............................................................... | 0.001 |
|  |  | Atomic Absorption; Platform—Stabilized Temperature ..................... | 0.0005 7 |
|  |  | Atomic Absorption; Gaseous Hydride ................................................ | 0.001 |
|  |  | ICP-Mass Spectrometry ..................................................................... | 0.0014 8 |
| Asbestos ............................. | 7 MFL 1 .... | Transmission Electron Microscopy .................................................... | 0.01 MFL |
| Barium ................................ | 2 ............... | Atomic Absorption; furnace technique ............................................... | 0.002 |
|  |  | Atomic Absorption; direct aspiration .................................................. | 0.1 |
|  |  | Inductively Coupled Plasma ............................................................... | 0.002 (0.001) |
| Beryllium ............................. | 0.004 ........ | Atomic Absorption; Furnace ............................................................... | 0.0002 |
|  |  | Atomic Absorption; Platform .............................................................. | 0.00002 5 |
|  |  | Inductively Coupled Plasma 2 ............................................................ | 0.0003 |
|  |  | ICP-Mass Spectrometry ..................................................................... | 0.0003 |
| Cadmium ............................ | 0.005 ........ | Atomic Absorption; furnace technique ............................................... | 0.0001 |
|  |  | Inductively Coupled Plasma ............................................................... | 0.001 |
| Chromium ........................... | 0.1 ............ | Atomic Absorption; furnace technique ............................................... | 0.001 |
|  |  | Inductively Coupled Plasma ............................................................... | 0.007 (0.001) |
| Cyanide ............................... | 0.2 ............ | Distillation, Spectrophotometric 3 ....................................................... | 0.02 |
|  | .................. | Distillation, Automated, Spectrophotometric 3 .................................... | 0.005 |
|  | .................. | Distillation, Amenable, Spectrophotometric 4 ..................................... | 0.02 |
|  | .................. | Distillation, Selective Electrode3 4 ...................................................... | 0.05 |
|  | .................. | UV, Distillation, Spectrophotometric 9 ................................................ | 0.0005 |
|  | .................. | Micro Distillation, Flow Injection, Spectrophotometric 3 ..................... | 0.0006 |
|  | .................. | Ligand Exchange with Amperometry 4 ............................................... | 0.0005 |
| Mercury ............................... | 0.002 ........ | Manual Cold Vapor Technique .......................................................... | 0.0002 |
|  |  | Automated Cold Vapor Technique ..................................................... | 0.0002 |
| Nickel .................................. | xl .............. | Atomic Absorption; Furnace ............................................................... | 0.001 |
|  |  | Atomic Absorption; Platform .............................................................. | 0.0006 5 |
|  |  | Inductively Coupled Plasma 2 ............................................................ | 0.005 |
|  |  | ICP-Mass Spectrometry ..................................................................... | 0.0005 |
| Nitrate ................................. | 10 (as N) | Manual Cadmium Reduction .............................................................. | 0.01 |
|  |  | Automated Hydrazine Reduction ....................................................... | 0.01 |
|  |  | Automated Cadmium Reduction ........................................................ | 0.05 |
|  |  | Ion Selective Electrode ...................................................................... | 1 |
|  |  | Ion Chromatography .......................................................................... | 0.01 |
|  |  | Capillary Ion Electrophoresis ............................................................. | 0.076 |
| Nitrite .................................. | 1 (as N) ... | Spectrophotometric ............................................................................ | 0.01 |
|  |  | Automated Cadmium Reduction ........................................................ | 0.05 |
|  |  | Manual Cadmium Reduction .............................................................. | 0.01 |
|  |  | Ion Chromatography .......................................................................... | 0.004 |
|  |  | Capillary Ion Electrophoresis ............................................................. | 0.103 |
| Selenium ............................. | 0.05 .......... | Atomic Absorption; furnace ................................................................ | 0.002 |
|  |  | Atomic Absorption; gaseous hydride ................................................. | 0.002 |
| Thallium .............................. | 0.002 ........ | Atomic Absorption; Furnace ............................................................... | 0.001 |
|  |  | Atomic Absorption; Platform .............................................................. | 0.0007 5 |
|  |  | ICP-Mass Spectrometry ..................................................................... | 0.0003 |

1 MFL = million fibers per liter >10 m.

2 Using  a  2X  preconcentration  step  as  noted  in  Method  200.7.  Lower  MDLs  may  be  achieved  when  using  a  4X preconcentration.

3 Screening method for total cyanides.

4 Measures ‘‘free’’ cyanides when distillation, digestion, or ligand exchange is omitted.

5 Lower MDLs are reported using stabilized temperature graphite furnace atomic absorption.

#### Environmental Protection Agency	§ 141.23

6 The value for arsenic is effective January 23, 2006. Unit then, the MCL is 0.05 mg/L.

7 The MDL reported for EPA method 200.9 (Atomic Absorption; Platform—Stablized Temperature) was determined using a 2x concentration step during sample digestion. The MDL determined for samples analyzed using direct analyses (i.e., no sample di- gestion) will be higher. Using multiple depositions, EPA 200.9 is capable of obtaining MDL of 0.0001 mg/L.

8 Using selective ion monitoring, EPA Method 200.8 (ICP-MS) is capable of obtaining a MDL of 0.0001 mg/L.

9 Measures total cyanides when UV-digestor is used, and ‘‘free’’ cyanides when UV-digestor is bypassed.

        - If the population served by the system is >3,300 persons, then compositing may only be permitted by the State at sampling points within a single system. In systems serving 3,300 persons, the State may permit compositing among different systems provided the 5-sample limit is main- tained.

        - If duplicates of the original sam- ple taken from each  sampling  point used in the composite sample are avail- able, the system may use these instead of resampling. The duplicates must be analyzed and the results reported to the State within 14 days after com- pleting analysis of the composite sam- ple, provided the holding time of the sample is not exceeded.

      - The frequency of monitoring for asbestos shall be in accordance with paragraph (b) of this section: the fre- quency of monitoring for antimony, ar- senic, barium, beryllium, cadmium, chromium, cyanide, fluoride, mercury, nickel, selenium and thallium  shall  be in accordance  with  paragraph  (c)  of this section; the frequency of moni- toring for nitrate shall be in accord- ance with paragraph (d) of this section; and the frequency of monitoring for ni- trite shall be in accordance with para- graph (e) of this section.

    - The frequency of monitoring con- ducted to determine compliance with the maximum contaminant level for asbestos specified in § 141.62(b) shall be conducted as follows:

      - Each community and non-tran- sient, non-community water system is required to monitor for asbestos during the first three-year compliance period of each nine-year compliance cycle be- ginning in the compliance period start- ing January 1, 1993.

      - If the system believes it is not vulnerable to either asbestos contami- nation in its source water or due to corrosion of asbestos-cement pipe, or both, it may apply to the State for a waiver of the monitoring requirement in paragraph (b)(1) of this section. If

the  State  grants  the  waiver,  the  sys- tem is not required to monitor.

      - The State may grant a waiver based on a consideration of the fol- lowing factors:

        - Potential asbestos contamination of the water source, and

        - The use of asbestos-cement pipe for finished water distribution and the corrosive nature of the water.

      - A waiver remains in effect until the completion of the three-year com- pliance period. Systems not receiving a waiver must monitor in accordance with the provisions of paragraph (b)(1) of this section.

      - A system vulnerable to asbestos contamination due solely to  corrosion of asbestos-cement pipe shall take one sample at a tap served by asbestos-ce- ment pipe and under conditions where asbestos contamination is most  likely to occur.

      - A system vulnerable to asbestos contamination due solely to source water shall monitor in accordance with the provision of paragraph (a) of this section.

      - A system vulnerable to asbestos contamination due both to its source water supply and corrosion of asbestos- cement pipe shall take one sample at a tap served by asbestos-cement pipe and under conditions where asbestos con- tamination is most likely to occur.

      - A system which exceeds the max- imum contaminant levels as deter- mined in § 141.23(i) of this section shall monitor quarterly beginning in the next quarter after the violation oc- curred.

      - The State may decrease the quar- terly monitoring requirement to the frequency specified in paragraph (b)(1) of this section provided the State has determined that the system is reliably and consistently below the maximum contaminant level. In no  case  can  a State make  this  determination  unless a groundwater system takes a min- imum of two quarterly samples and a surface  (or  combined  surface/ground)

#### § 141.23

water system takes a minimum of four quarterly samples.

      - If monitoring data collected after January 1, 1990 are generally con- sistent     with     the     requirements     of

§ 141.23(b), then the State may allow systems to use that data to satisfy the monitoring requirement for the initial compliance  period  beginning   January 1, 1993.

    - The frequency of monitoring con- ducted to determine compliance with the  maximum  contaminant  levels  in

§ 141.62 for antimony, arsenic, barium, beryllium, cadmium, chromium, cya- nide, fluoride, mercury, nickel, sele- nium  and  thallium  shall  be  as  follows:

      - Groundwater systems shall take one sample at each sampling point dur- ing each compliance period. Surface water systems (or combined surface/ ground) shall take one sample annually at each sampling point.

      - The system may apply to the State for a waiver from the monitoring frequencies specified in paragraph (c)(1) of this section. States may grant a public water system a waiver for moni- toring of cyanide, provided that the State determines that the system is not vulnerable due to lack of any in- dustrial source of cyanide.

      - A condition of the waiver shall re- quire that a system shall take a min- imum of one sample while the waiver is effective. The term during which the waiver is effective shall not exceed one compliance cycle (i.e., nine years).

      - The State may grant a waiver pro- vided surface water systems have mon- itored annually for at least three years and groundwater systems have con- ducted a minimum of three rounds of monitoring. (At least one sample shall have been taken since January 1, 1990). Both surface and groundwater systems shall demonstrate that all previous an- alytical results were less than the max- imum contaminant level. Systems that use a new water source are not eligible for a waiver until three rounds of mon- itoring from the new source have been completed.

      - In determining the appropriate re- duced monitoring frequency, the State shall consider:

        - Reported concentrations from all previous monitoring;

#### 40 CFR Ch. I (7–1–17 Edition)

        - The degree of variation in re- ported concentrations; and

        - Other factors which  may affect contaminant concentrations such as changes in groundwater pumping rates, changes in the system’s configuration, changes in the system’s operating pro- cedures, or changes in stream flows or characteristics.

      - A decision by the State to grant a waiver shall be made in writing and shall set forth the basis for the deter- mination. The determination may be initiated by the State or upon an appli- cation by the public water system. The public water system shall specify the basis for its request. The State shall review and, where appropriate, revise its determination of the appropriate monitoring frequency when the system submits new monitoring data or when other data relevant to the system’s ap- propriate monitoring frequency be- come available.

      - Systems which exceed the max- imum contaminant levels as  calculated in § 141.23(i) of this section shall mon- itor quarterly beginning in the next quarter after the violation occurred.

      - The State may decrease the quar- terly monitoring requirement to the frequencies specified in paragraphs (c)(1) and (c)(2) of this section provided it has determined that the system is reliably and consistently below the maximum contaminant level. In no case can a State make this determina- tion unless a groundwater system takes a minimum of two quarterly samples and a surface water system takes a minimum of four quarterly samples.

      - All new systems or systems that use a new source of water that begin operation after January 22, 2004 must demonstrate compliance with the MCL within a period of time specified by the State. The system must  also  comply with the initial sampling frequencies specified by the State to ensure a sys- tem can demonstrate compliance with the MCL. Routine and increased moni- toring frequencies shall be  conducted in accordance with the requirements in this  section.

    - All public water systems (commu- nity;   non-transient,   non-community;

#### Environmental Protection Agency	§ 141.23

and transient,  non-community  sys- tems) shall monitor to determine com- pliance  with  the  maximum  contami- nant level for nitrate in § 141.62.

      - Community and non-transient, non-community water  systems  served by groundwater systems shall monitor annually beginning January 1, 1993; systems served by surface water shall monitor   quarterly   beginning    January 1, 1993.

      - For community and non-tran- sient, non-community water  systems, the repeat monitoring frequency for groundwater systems shall be quar- terly for at least one year following any one sample in which the con- centration is 50 percent of the MCL. The State may allow a groundwater system to reduce the sampling fre- quency to annually after  four consecu- tive quarterly samples are reliably and consistently  less  than  the  MCL.

      - For community and non-tran- sient, non-community water  systems, the State may allow a surface water system to reduce the sampling fre- quency to annually if all analytical re- sults from four  consecutive  quarters are <50 percent of the MCL. A surface water system shall return to quarterly monitoring if any one sample is 50 percent of the MCL.

      - Each transient non-community water system shall monitor annually beginning January 1, 1993.

      - After the initial round of quar- terly sampling is completed, each com- munity and non-transient non-commu- nity system which is monitoring annu- ally shall take subsequent samples dur- ing the quarter(s) which previously re- sulted in the highest analytical result.

    - All public water systems (commu- nity;  non-transient,  non-community; and transient, non-community sys- tems) shall monitor to determine com- pliance with the maximum contami- nant level for nitrite in § 141.62(b).

      - All  public  water  systems   shall take  one  sample  at  each   sampling point in the compliance period begin- ning January 1, 1993 and ending Decem- ber 31, 1995.

      - After the initial sample, systems where an analytical result for nitrite is

<50 percent of the MCL shall monitor at the frequency specified by the State.

      - For community, non-transient, non-community, and transient non- community water systems, the repeat monitoring frequency for any water system shall be quarterly for at least one year following any one sample in which the concentration is 50 percent of the MCL. The State may allow a sys- tem to reduce the  sampling  frequency to annually after determining the sys- tem is reliably and  consistently  less than  the  MCL.

      - Systems which are monitoring an- nually shall take each subsequent sam- ple during the quarter(s) which pre- viously resulted in the highest analyt- ical result.

    - Confirmation  samples:

      - Where the results of sampling for antimony, arsenic, asbestos, barium, beryllium, cadmium, chromium, cya- nide, fluoride, mercury, nickel, sele- nium or thallium indicate an exceed- ance of the maximum contaminant level, the State may require that one additional sample be collected as soon as possible after the initial sample was taken (but not to exceed two weeks) at the same sampling point.

      - Where nitrate or nitrite sampling results indicate an exceedance of the maximum contaminant level, the sys- tem shall take a confirmation sample within 24 hours of the system’s receipt of notification of the  analytical  results of the first sample. Systems unable to comply with the 24-hour sampling re- quirement must immediately notify persons served by the public water sys- tem in accordance with § 141.202 and meet other Tier 1 public notification requirements under subpart Q of this part. Systems exercising this option must take and analyze a confirmation sample within two weeks of notifica- tion of  the  analytical  results  of  the first  sample.

      - If a State-required confirmation sample is taken for any contaminant, then the results of the initial and con- firmation sample shall be averaged. The resulting average shall be used to determine the system’s compliance in accordance with paragraph (i) of this section. States have the discretion to delete results of obvious sampling er- rors.

    - The State may require more fre- quent   monitoring   than   specified   in

#### § 141.23

paragraphs (b), (c), (d) and (e) of this section or may require confirmation samples for positive and negative re- sults at its  discretion.

    - Systems may apply to  the  State to conduct more frequent monitoring than the minimum monitoring fre- quencies specified in this section.

- Compliance	with	§ 141.11	or

§ 141.62(b) (as appropriate) shall be de- termined based on the analytical re- sult(s) obtained at  each  sampling point.

- For systems which are conducting monitoring at a frequency greater than annual, compliance with the maximum contaminant levels for antimony, ar- senic, asbestos, barium, beryllium, cad- mium, chromium, cyanide, fluoride, mercury, nickel, selenium or thallium is determined by a running annual av- erage at any sampling point. If the av- erage at any sampling point is greater than the MCL, then the system is out of compliance. If any one sample would cause the annual average to be exceed- ed, then the system is out of compli- ance immediately. Any sample below the method detection limit shall be calculated at zero for the purpose of de- termining the annual average. If a sys- tem fails to collect the required num- ber of samples, compliance (average concentration) will be based on the total number of samples collected.

- For systems which are monitoring annually, or less frequently, the sys- tem is out of compliance with the max- imum contaminant levels for anti- mony, arsenic, asbestos, barium, beryl- lium, cadmium, chromium, cyanide, fluoride, mercury, nickel, selenium or thallium if the level of a contaminant is greater than the MCL. If confirma- tion samples are required by the State, the  determination  of  compliance  will

#### 40 CFR Ch. I (7–1–17 Edition)

be based on the annual average of the initial MCL exceedance and any State- required confirmation samples. If a system fails to collect the required number of samples, compliance (aver- age concentration) will be based on the total number of samples collected.

- Compliance with the maximum contaminant levels for nitrate and ni- trate is determined based on one sam- ple if the levels of these contaminants are below the MCLs. If the levels of ni- trate and/or nitrite exceed the MCLs in the initial sample, a confirmation sam- ple is required in accordance with para- graph (f)(2) of this section, and compli- ance shall be determined based on the average of the initial and confirmation samples.

- Arsenic sampling results will be reported to the nearest 0.001 mg/L.

- Each public water system shall monitor at the time designated by the State during each compliance period.

- Inorganic analysis:

  - Analysis for the following con- taminants shall be conducted in ac- cordance with the methods in the fol- lowing table,  or  the  alternative  meth- ods listed in appendix A to subpart C of this part, or their equivalent as deter- mined by EPA. Criteria for analyzing arsenic, barium, beryllium, cadmium, calcium,  chromium,  copper,  lead,   nick- el,   selenium,   sodium,   and   thallium with digestion or directly without di- gestion, and other analytical test pro- cedures are  contained  in  Technical Notes on Drinking Water Methods, EPA– 600/R–94–173, October 1994. This docu- ment is available from the National Service Center for Environmental Pub- lications (NSCEP), P.O. Box 42419, Cin- cinnati, OH 45242–0419

Environmental Protection Agency

§ 141.23

409

| Contaminant | Methodology 13 | EPA | ASTM 3 | SM 4 (18th, 19th ed.) | SM 4 (20th ed.) | SM Online 22 | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1. Alkalinity .................. 2. Antimony ................. 3. Arsenic 14 ................. 4. Asbestos ................. 5. Barium ..................... 6. Beryllium ................. 7. Cadmium ................. | Titrimetric ....................... Electrometric titration ..... Inductively Coupled Plasma (ICP)—Mass Spectrometry. Hydride-Atomic Absorp- tion. Atomic Absorption; Plat- form. Atomic Absorption; Fur- nace. ICP-Mass Spectrometry Atomic Absorption; Plat- form. Atomic Absorption; Fur- nace. Hydride Atomic Absorp- tion. Transmission Electron Microscopy. Transmission Electron Microscopy. Inductively Coupled Plasma. ICP-Mass Spectrometry Atomic Absorption; Di- rect. Atomic Absorption; Fur- nace. Inductively Coupled Plasma. ICP-Mass Spectrometry Atomic Absorption; Plat- form. Atomic Absorption; Fur- nace. Inductively Coupled Plasma. ICP-Mass Spectrometry Atomic Absorption; Plat- form. | ....................... ....................... 200.8 2 ....................... 200.9 2 ....................... 200.8 2. 200.9 2. ....................... ....................... 100.1 9 100.2 10 200.7 2 .......... 200.8 2 ....................... ....................... 200.7 2 .......... 200.8 2 200.9 2 ....................... 200.7 2 200.8 2 200.9 2 | D1067–92, 02 B ............ ........................................ D3697–92, 02. ........................................ D2972–97, 03 C ............ D1972–97, 03 B ............ ........................................ ........................................ ........................................ ........................................ D3645–97, 03 B ............ | 2320 B .......... ....................... 3113 B .......... 3113 B .......... 3114 B .......... 3120 B .......... 3111D ........... 3113 B .......... 3120 B .......... 3113 B .......... | 2320 B .......... ....................... ....................... ....................... ....................... 3120 B .......... ....................... ....................... 3120 B .......... ....................... | 2320 B–97. I–1030–85 5. 3113 B–99. 3113 B–99. 3114 B–97. 3120 B–99. 3111 D–99. 3113 B–99. 3120 B–99. 3113 B–99. |  |

§ 141.23

40 CFR Ch. I (7–1–17 Edition)

410

| Contaminant | Methodology 13 | EPA | ASTM 3 | SM 4 (18th, 19th ed.) | SM 4 (20th ed.) | SM Online 22 | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 8. Calcium ................... 9. Chromium ................ 10. Copper .................. 11. Conductivity ........... 12. Cyanide ................. | Atomic Absorption; Fur- nace. EDTA titrimetric ............. Atomic Absorption; Di- rect Aspiration. Inductively Coupled Plasma. Ion Chromatography ...... Inductively Coupled Plasma. ICP-Mass Spectrometry Atomic Absorption; Plat- form. Atomic Absorption; Fur- nace. Atomic Absorption; Fur- nace. Atomic Absorption; Di- rect Aspiration. Inductively Coupled Plasma. ICP-Mass spectrometry Atomic Absorption; Plat- form. Conductance .................. Manual Distillation fol- lowed by Spectrophotometric, Amenable. Spectro-photometric Manual. Spectro-photometric Semi-automated. Selective Electrode ........ UV, Distillation, Spectrophotometric. | ....................... ....................... ....................... 200.7 2 .......... ....................... 200.7 2 .......... 200.8 2 200.9 2 ....................... ....................... ....................... 200.7 2 .......... 200.8 2 200.9 2 ....................... ....................... ....................... ....................... 335.4 6 ....................... ....................... | ........................................ D511–93, 03 A .............. D511–93, 03 B .............. ........................................ D6919–03. ........................................ ........................................ D1688–95, 02 C ............ D1688–95, 02 A ............ ........................................ D1125–95 (Reapproved 1999) A. D2036–98 A ................... D2036–98 B ................... D2036–98 A ................... ........................................ ........................................ | 3113 B .......... 3500–Ca D ... 3111 B .......... 3120 B .......... 3120 B .......... 3113 B .......... 3113 B .......... 3111 B .......... 3120 B .......... 2510 B .......... 4500–CN¥ C 4500–CN¥ G 4500–CN¥ E 4500–CN¥ F ....................... | ....................... 3500–Ca B ... ....................... 3120 B .......... 3120 B .......... ....................... ....................... ....................... 3120 B .......... 2510 B .......... 4500–CN¥ C. 4500–CN¥ G 4500–CN¥ E 4500–CN¥ F ....................... | 3113 B–99. 3500–Ca B– 97. 3111 B–99. 3120 B–99. 3120 B–99. 3113 B–99. 3113 B–99. 3111 B–99. 3120 B–99. 2510 B–97. 4500–CN¥ G–99. 4500–CN¥ E–99. 4500–CN¥ F–99. ....................... | I–3300–85 5 Kelada–01 17 |

Micro Distillation, Flow Injection, Spectrophotometric.

Ligand Exchange and Amperometry 21.

.......................    ........................................    .......................    .......................    .......................   QuikChem

Environmental Protection Agency

10–204–

00–1–X 18

.......................   D6888–04 ......................    .......................    .......................    .......................   OIA–1677,

DW 20

13. Fluoride  .................   Ion Chromatography ......   300.0 6,

300.1 19

D4327–97, 03 ................   4110 B ..........   4110 B ..........   4110 B–00.

Manual Distill.; Color. SPADNS.

.......................    ........................................   4500–F¥ B,

D.

4500–F¥ B, D.

4500–F¥ B, D–97.

Manual Electrode ...........    .......................   D1179–93, 99 B  ............   4500–F¥ C ...   4500–F¥ C ...   4500–F¥ C–

97.

Automated Electrode .....    .......................    ........................................    .......................    .......................    .......................   380–75WE 11

Automated Alizarin  ........    .......................    ........................................   4500–F¥ E ...   4500–F¥ E ...   4500–F¥ E–

97.

129–71W 11

Capillary Ion Electro- phoresis.

14. Lead ......................   Atomic Absorption; Fur-

nace.

.......................    ........................................    .......................    .......................    .......................   D6508, Rev.

2 23

.......................   D3559–96, 03 D ............   3113 B ..........    .......................   3113 B–99.

ICP–Mass spectrometry	200.8 2

Atomic Absorption; Plat- form.

Differential Pulse Anodic Stripping Voltametry.

200.9 2

.......................    ........................................    .......................    .......................    .......................   Method

1001 16

15. Magnesium ............   Atomic Absorption  .........    .......................   D511–93, 03 B  ..............   3111 B ..........    .......................   3111 B–99.

ICP .................................   200.7 2   ..........    ........................................   3120 B ..........   3120 B ..........   3120 B–99.

Complexation Titrimetric Methods.

.......................   D511–93, 03 A  ..............   3500–Mg E ...   3500–Mg B ...   3500–Mg B–

97.

Ion Chromatography ......    .......................   D6919–03.

16. Mercury .................   Manual, Cold Vapor .......   245.1 2   ..........   D3223–97, 02 ................   3112 B ..........    .......................   3112 B–99.

Automated, Cold Vapor	245.2 1

ICP–Mass Spectrometry   200.8 2

17. Nickel  ....................   Inductively Coupled

Plasma.

200.7 2   ..........    ........................................   3120 B ..........   3120 B ..........   3120 B–99.

ICP–Mass Spectrometry   200.8 2

Atomic Absorption; Plat- form.

Atomic Absorption; Di- rect.

Atomic Absorption; Fur- nace.

200.9 2

.......................    ........................................   3111 B ..........    .......................   3111 B–99.

.......................    ........................................   3113 B ..........    .......................   3113 B–99.

18. Nitrate ....................   Ion Chromatography ......   300.0 6,

300.1 19

D4327–97, 03 ................   4110 B ..........   4110 B ..........   4110 B–00 ....   B–1011 8

§ 141.23

¥ F   4500–NO ¥ F   4500–NO ¥

Automated Cadmium

Reduction.

353.2 6   ..........   D3867–90 A ...................   4500–NO3

3	3

F–00

411

§ 141.23

40 CFR Ch. I (7–1–17 Edition)

412

| Contaminant | Methodology 13 | EPA | ASTM 3 | SM 4 (18th, 19th ed.) | SM 4 (20th ed.) | SM Online 22 | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 19. Nitrite ..................... 20. Ortho-phosphate ... 21. pH .......................... 22. Selenium ............... 23. Silica ...................... | Ion Selective Electrode .. Manual Cadmium Re- duction. Capillary Ion Electro- phoresis. Ion Chromatography ...... Automated Cadmium Reduction. Manual Cadmium Re- duction. Spectrophotometric ........ Capillary Ion Electro- phoresis. Colorimetric, Automated, Ascorbic Acid. Colorimetric, ascorbic acid, single reagent. Colorimetric Phosphomolybdate; Automated-segmented flow; Automated Dis- crete. Ion Chromatography ...... Capillary Ion Electro- phoresis. Electrometric .................. Hydride-Atomic Absorp- tion. ICP–Mass Spectrometry Atomic Absorption; Plat- form. Atomic Absorption; Fur- nace. Colorimetric, Molybdate Blue. | ....................... ....................... ....................... 300.0 6, 300.1 19. 353.2 6 .......... ....................... ....................... ....................... 365.1 6 .......... ....................... ....................... 300.0 6, 300.1 19. ....................... 150.1, 150.2 1 ....................... 200.8 2 200.9 2 ....................... ....................... | ........................................ D3867–90 B ................... D6508–00. D4327–97, 03 ................ D3867–90 A ................... D3867–90 B ................... ........................................ D6508–00 ........................................ D515–88 A ..................... ........................................ D4327–97, 03 ................ D6508–00 D1293–95, 99 ................ D3859–98, 03 A ............ D3859–98, 03 B ............ ........................................ | 4500–NO ¥ 3 D. 4500–NO ¥ E 3 4110 B .......... 4500–NO ¥ F 3 4500–NO ¥ E 3 4500–NO ¥ B 2 4500–P F ...... 4500–P E ...... ....................... 4110 B .......... 4500–H + B. 3114 B .......... 3113 B .......... ....................... | 4500–NO ¥ 3 D. 4500–NO ¥ E 3 4110 B .......... 4500–NO ¥ F 3 4500–NO ¥ E 3 4500–NO ¥ B 2 4500–P F 4500–P E ....................... 4110 B .......... 4500–H + B. ....................... ....................... ....................... | 4500–NO ¥ 3 D–00. 4500–NO ¥ 3 E–00 4110 B–00 .... 4500–NO ¥ 3 F–00 4500–NO ¥ 3 E–00 4500–NO ¥ 2 B–00 ....................... 4110 B–00 4500–H + B–00. 3114 B–97. 3113 B–99. ....................... | 601 7 B–1011 8 I–1601–85 5 I–2601–90 5 I–2598–85 5 I–1700–85 5 |

413

Automated-seg-

mented Flow.

Colorimetric .................... Molybdosilicate ..............

.......................

........................................    .......................    .......................    .......................   I–2700–85 5

.......................

.......................

D859–94, 00.

........................................

4500–Si D .....

4500–SiO2  C

Heteropoly blue  .............    .......................    ........................................   4500–Si E .....   4500–SiO2  D

25. Temperature ..........

26. Thallium .................

Automated for Molyb-

date-reactive Silica. Inductively Coupled

Plasma. Inductively Coupled

Plasma.

Atomic Absorption; Di- rect Aspiration.

Ion Chromatography ...... Thermometric ................. ICP–Mass Spectrometry Atomic Absorption; Plat-

form.

.......................    ........................................   4500–Si F .....   4500–SiO2  E

200.7 2  ..........

........................................

3120 B ..........

3120 B ..........

4500–SiO2  C–

97.

4500–SiO2  D–

97.

4500–SiO2  E–

97.

3120 B–99.

24. Sodium ..................

200.7 2

.......................

........................................

3111 B ..........

.......................

3111 B–99.

.......................

.......................

200.8 2

200.9 2.

D6919–03.

........................................

2550 ..............

2550 ..............

2550–00.

Environmental Protection Agency

The procedures shall be done in accordance with the documents listed below. The incorporation by reference of the following documents listed in footnotes 1–11, 16–20, and 22–23 was approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies of the documents may be obtained from the sources listed below. Information regarding obtaining these documents can be obtained from the Safe Drinking Water Hotline at 800–426–4791. Documents may be inspected at EPA’s Drinking Water Docket, EPA West, 1301 Constitution Avenue, NW., Room 3334, Washington, DC 20460 (Telephone: 202–566–2426); or at the National Archives and Records Administration (NARA). For infor- mation  on  the  availability  of  this  material  at  NARA,  call  202–741–6030

1 ‘‘Methods for Chemical Analysis of Water and Wastes,’’ EPA/600/4–79/020, March 1983. Available at NTIS, PB84–128677.

2 ‘‘Methods for the Determination of Metals in Environmental Samples—Supplement I,’’ EPA/600/R–94/111, May 1994. Available at NTIS, PB95–125472.

3 Annual Book of ASTM Standards, ASTM International, 100 Barr Harbor Drive, West Conshohocken, PA 19428,; Annual Book of ASTM Standards 1994, Vols.

11.01 and 11.02; Annual Book of ASTM Standards 1996, Vols. 11.01 and 11.02; Annual Book of ASTM Standards 1999, Vols. 11.01 and 11.02; Annual Book of ASTM Standards 2003, Vols. 11.01 and 11.02.

4 Standard Methods for the Examination of Water and Wastewater, American Public Health Association, 800 I Street NW., Washington, DC 20001–3710; Standard Methods for the Ex- amination of Water and Wastewater, 18th edition (1992); Standard Methods for the Examination of Water and Wastewater, 19th edition (1995); Standard Methods for the Examination of Water and Wastewater, 20th edition (1998).The following methods from this edition cannot be used: 3111 B, 3111 D, 3113 B, and 3114 B.

5 U.S. Geological Survey, Federal Center, Box 25286, Denver, CO 80225–0425; Methods for Analysis by the U.S. Geological Survey National Water Quality Laboratory—Determination of Inorganic and Organic Constituents in Water and Fluvial Sediment, Open File Report 93–125, 1993; Techniques of Water Resources Investigation of the U.S. Geological Survey, Book 5, Chapter A–1, 3rd edition, 1989.

6 ‘‘Methods for the Determination of Inorganic Substances in Environmental Samples,’’ EPA/600/R–93/100, August 1993. Available as Technical Report PB94–120821 at National Tech- nical Information Service (NTIS), 5301 Shawnee Road, Alexandria, VA 22312.

7 The procedure shall be done in accordance with the Technical Bulletin 601 ‘‘Standard Method of Test for Nitrate in Drinking Water,’’ July 1994, PN 221890–001, Analytical Tech- nology, Inc. Copies may be obtained from ATI Orion, 529 Main Street, Boston, MA 02129.

8 Method B–1011. ‘‘Waters Test Method for Determination of Nitrite/Nitrate in Water Using Single Column Ion Chromatography,’’ August, 1987. Copies may be obtained from Waters Corporation, Technical Services Division, 34 Maple Street, Milford, MA 01757, Telephone: 508/482–2963, Fax: 508/482–4056.

9 Method 100.1, ‘‘Analytical Method For Determination of Asbestos Fibers in Water,’’ EPA/600/4–83/043, EPA, September 1983. Available at NTIS, PB83–260471.

10 Method 100.2, ‘‘Determination of Asbestos Structure Over 10-m In Length In Drinking Water,’’ EPA/600/R–94/134, June 1994. Available at NTIS, PB94–201902.

§ 141.23

11 Industrial Method No. 129–71W, ‘‘Fluoride in Water and Wastewater,’’ December 1972, and Method No. 380–75WE, ‘‘Fluoride in Water and Wastewater,’’ February 1976, Technicon Industrial Systems. Copies may be obtained from Bran & Luebbe, 1025 Busch Parkway, Buffalo Grove, IL 60089.

12 Unfiltered, no digestion or hydrolysis.

13 Because MDLs reported in EPA Methods 200.7 and 200.9 were determined using a 2x preconcentration step during sample digestion, MDLs determined when samples are analyzed by direct analysis (i.e., no sample digestion) will be higher. For direct analysis of cadmium and arsenic by Method 200.7, and arsenic by Method 3120 B, sample preconcentration using pneumatic nebulization may be required to achieve lower detection limits. Preconcentration may also be required for direct analysis of antimony, lead, and thallium by Method 200.9; anti- mony and lead by Method 3113 B; and lead by Method D3559–90D, unless multiple in-furnace depositions are made.

40 CFR Ch. I (7–1–17 Edition)

414

§ 141.23

14 If ultrasonic nebulization is used in the determination of arsenic by Method 200.8, the arsenic must be in the pentavalent state to provide uniform signal response. For direct analysis of arsenic with Method 200.8 using ultrasonic nebulization, samples and standards must contain 1 mg/L of sodium hypochlorite.

15 [Reserved]

16 The description for Method Number 1001 for lead is available from Palintest, LTD, 21 Kenton Lands Road, P.O. Box 18395, Erlanger, KY 41018. Or from the Hach Company, P.O. Box 389, Loveland, CO 80539.

17 The description for the Kelada-01 Method, ‘‘Kelada Automated Test Methods for Total Cyanide, Acid Dissociable Cyanide, And Thiocyanate,’’ Revision 1.2, August 2001, EPA # 821– B–01–009 for cyanide is available from the National Technical Information Service (NTIS), PB 2001–108275, 5285 Port Royal Road, Springfield, VA 22161. The toll free telephone num- ber is 800–553–6847. Note: A 450–W UV lamp may be used in this method instead of the 550–W lamp specified if it provides performance within the quality control (QC) acceptance criteria of the method in a given instrument. Similarly, modified flow cell configurations and flow conditions may be used in the method, provided that the QC acceptance criteria are met.

18 The description for the QuikChem Method 10–204–00–1–X, ‘‘Digestion and distillation of total cyanide in drinking and wastewaters using MICRO DIST and determination of cyanide by flow injection analysis,’’ Revision 2.1, November 30, 2000, for cyanide is available from Lachat Instruments, 6645 W. Mill Rd., Milwaukee, WI 53218. Telephone: 414–358–4200.

19 ‘‘Methods for the Determination of Organic and Inorganic Compounds in Drinking Water,’’ Vol. 1, EPA 815–R–00–014, August 2000. Available as Technical Report PB2000–106981 at National Technical Information Service (NTIS), 5301 Shawnee Road, Alexandria, VA 22312. .

20 Method OIA–1677, DW ‘‘Available Cyanide by Flow Injection, Ligand Exchange, and Amperometry,’’ January 2004. EPA–821–R–04–001, Available from ALPKEM, A Division of OI Analytical, P.O. Box 9010, College Station, TX 77842–9010.

21 Sulfide levels below those detected using lead acetate paper may produce positive method interferences. Test samples using a more sensitive sulfide method to determine if a sul- fide interference is present, and treat samples accordingly.

22 Standard Methods Online, American Public Health Association, 800 I Street NW., Washington, DC 20001, The year in which each meth- od was approved by the Standard Methods Committee is designated by the last two digits in the method number. The methods listed are the only online versions that may be used.

#### Environmental Protection Agency	§ 141.23

| Contaminant | Preservative 1 | Con- tainer 2 | Time 3 |
| --- | --- | --- | --- |
| Antimony ......... | HNO3 .............. | P or G ..... | 6 months |
| Arsenic ............ | Conc HNO3 to | P or G ..... | 6 months |
|  | pH <2. |  |  |
| Asbestos ......... | 4 C ................. | P or G ..... | 48 hours 4 |
| Barium ............. | HNO3 .............. | P or G ..... | 6 months |
| Beryllium ......... | HNO3 .............. | P or G ..... | 6 months |
| Cadmium ......... | HNO3 .............. | P or G ..... | 6 months |
| Chromium ........ | HNO3 .............. | P or G ..... | 6 months |
| Cyanide ........... | 4 C, NaOH .... | P or G ..... | 14 days |
| Fluoride ........... | None ............... | P or G ..... | 1 month |
| Mercury ........... | HNO3 .............. | P or G ..... | 28 days |
| Nickel .............. | HNO3 .............. | P or G ..... | 6 months |
| Nitrate .............. | 4 C ................. | P or G ..... | 48 hours 5 |
| Nitrate-Nitrite 6 | H2SO4 ............. | P or G ..... | 28 days |
| Nitrite ............... | 4 C ................. | P or G ..... | 48 hours |
| Selenium ......... | HNO3 .............. | P or G ..... | 6 months |
| Thallium ........... | HNO3 .............. | P or G ..... | 6 months |

Sample collection for antimony, arsenic, asbestos, barium, beryllium, cadmium, chromium, cyanide, fluoride, mercury, nickel, nitrate, nitrite, sele- nium, and thallium under this section shall be conducted using the sample preservation, container, and maximum holding time procedures specified in the table below:

| Contaminant | Acceptance limit |
| --- | --- |
| Antimony ............................... | 30 at 0.006 mg/1 |
| Arsenic .................................. | 30 at 0.003 mg/L |
| Asbestos ............................... | 2 standard deviations based |
|  | on study statistics. |
| Barium .................................. | 15% at 0.15 mg/1 |
| Beryllium ............................... | 15% at 0.001 mg/1 |
| Cadmium .............................. | 20% at 0.002 mg/1 |
| Chromium ............................. | 15% at 0.01 mg/1 |
| Cyanide ................................ | 25% at 0.1 mg/1 |
| Fluoride ................................. | 10% at 1 to 10 mg/1 |
| Mercury ................................. | 30% at 0.0005 mg/1 |
| Nickel .................................... | 15% at 0.01 mg/1 |
| Nitrate ................................... | 10% at 0.4 mg/1 |
| Nitrite .................................... | 15% at 0.4 mg/1 |
| Selenium ............................... | 20% at 0.01 mg/1 |
| Thallium ................................ | 30% at 0.002 mg/1 |

For each contaminant that has been included in the PE sample and for each method for which the laboratory desires certification achieve quan- titative results on the analyses that are within the following acceptance limits:

1 For cyanide determinations samples must be adjusted with sodium hydroxide to pH 12 at the time off collection. When chilling is indicated the sample must be shipped and stored at 4 C or less. Acidification of nitrate or metals samples may be with a concentrated acid or a dilute (50% by volume) solution of the applicable concentrated acid. Acidification of samples for metals analysis is encouraged and allowed at the labora- tory rather than at the time of sampling provided the shipping time and other instructions in Section 8.3 of EPA Methods

200.7 or 200.8 or 200.9 are followed.

2 P = plastic, hard or soft; G = glass, hard or soft.

3 In all cases samples should be analyzed as soon after col- lection as possible. Follow additional (if any) information on preservation, containers or holding times that is specified in method.

4 Instructions for containers, preservation procedures and holding times as specified in Method 100.2 must be adhered to for all compliance analyses including those conducted with Method 100.1.

5 If the sample is chlorinated, the holding time for an unacidified sample kept at 4 C is extended to 14 days.

6 Nitrate-Nitrite refers to a measurement of total nitrate.

  - Analysis under this section shall only be conducted by laboratories that have been certified by EPA or the State. Laboratories may conduct sam- ple analysis under provisional certifi- cation until January 1, 1996. To receive certification to conduct analyses for antimony, arsenic, asbestos, barium, beryllium, cadmium, chromium, cya- nide, fluoride, mercury, nickel, nitrate, nitrite and selenium and thallium, the laboratory must:

    - Analyze Performance Evaluation (PE) samples provided by EPA, the State or by a third party (with the ap- proval of the State or EPA) at least once a year.

- Analyses for the purpose of deter- mining compliance with § 141.11 shall be conducted using the requirements spec- ified in  paragraphs  (l)  through  (q)  of this   section.

  - Analyses for all community water systems utilizing surface water sources shall be completed by June 24, 1978. These analyses shall be repeated at yearly   intervals.

  - Analyses for all community water systems utilizing only ground water sources shall be completed by June 24, 1979. These analyses shall be repeated at  three-year  intervals.

  - For non-community water sys- tems, whether supplied by surface or ground sources, analyses for nitrate shall be completed by December 24, 1980. These analyses shall be repeated at intervals determined by the State.

  - The State has the authority to de- termine compliance or initiate enforce- ment action based upon analytical re- sults and other information compiled by their sanctioned representatives and agencies.

- If the result of an analysis made under paragraph (l) of this section indi- cates that the level of any contami- nant listed in § 141.11 exceeds the max- imum contaminant level, the  supplier of the water shall report to the State within 7 days and initiate three addi- tional analyses at the same sampling point within one month.

#### § 141.24

- When the average of four analyses made pursuant to paragraph (m) of this section, rounded to the same number of significant figures as the maximum contaminant level for the substance in question, exceeds the maximum con- taminant level, the supplier of water shall   notify   the   State   pursuant   to

§ 141.31 and give notice to the public pursuant   to   subpart   Q.   Monitoring after public notification shall be at a frequency designated by the State and shall continue until the maximum con- taminant level  has  not  been   exceeded in two successive samples or until a monitoring schedule as a condition to a variance, exemption or  enforcement action  shall  become  effective.

- The provisions of paragraphs (m) and (n) of this section notwithstanding, compliance with the maximum con- taminant level for nitrate shall be de- termined on the basis of the mean  of two  analyses.  When  a  level  exceeding the maximum contaminant level for nitrate is found, a second  analysis  shall be initiated within 24 hours, and if the mean of the two analyses exceeds the maximum contaminant level, the sup- plier of water shall  report  his  findings to the State pursuant to § 141.31 and shall notify the public pursuant to sub- part  Q.

- For the initial analyses required by paragraph  (l) (1), (2) or  (3) of this section, data for surface waters ac- quired within one year prior to the ef- fective date and data for ground waters acquired within 3 years prior to the ef- fective date of this part may be sub- stituted  at  the  discretion  of  the  State.

- [Reserved]

[56 FR 3579, Jan. 30, 1991]

EDITORIAL NOTE: For FEDERAL REGISTER ci-

tations affecting § 141.23, see the List of CFR Sections Affected, which appears in  the Finding Aids  section of  the printed volume

##### § 141.24   Organic   chemicals,   sampling and analytical requirements.

(a)–(d) [Reserved]

- Analyses for the contaminants in this section shall be conducted using the methods listed in the following table, or the alternative methods listed in appendix A to subpart C of this part, or their equivalent as determined by EPA.

#### 40 CFR Ch. I (7–1–17 Edition)

- The following documents are in- corporated by reference. This incorpo- ration by reference was approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies may be inspected at EPA’s Drinking Water Docket, 1301 Constitution  Avenue,  NW.,  EPA  West, Room 3334, Washington, DC 20460 (Tele- phone: 202–566–2426); or at the National Archives  and  Records  Administration (NARA). For information on the avail- ability  of  this  material  at  NARA,  call 202–741–6030.   Method   508A    and

515.1 are in Methods for the Determina- tion of Organic Compounds in Drinking Water, EPA/600/4–88–039, December 1988, Revised, July 1991. Methods 547, 550 and

550.1 are in Methods for the Determina- tion of Organic Compounds in Drinking Water—Supplement I, EPA/600–4–90–020, July 1990. Methods 548.1, 549.1, 552.1 and 555 are in  Methods  for  the  Determination of Organic Compounds in Drinking Water—Supplement II, EPA/600/R–92–129, August 1992. Methods 502.2, 504.1, 505, 506, 507, 508, 508.1, 515.2, 524.2 525.2, 531.1,

551.1 and 552.2 are in Methods for the De- termination of Organic Compounds in Drinking Water––Supplement III, EPA/ 600/R–95–131, August 1995. Method 1613 is titled  ‘‘Tetra-through  Octa- Chlorinated Dioxins and Furans by Iso- tope-Dilution HRGC/HRMS,’’ EPA/821– B–94–005, October 1994. These docu- ments are available from the National Technical Information Service, NTIS PB91–231480, PB91–146027, PB92–207703, PB95–261616 and PB95–104774, U.S. De- partment  of  Commerce,   5285   Port Royal Road, Springfield, Virginia 22161. The toll free number is: 800–553–6847. Method 6651 shall be followed in ac- cordance with Standard Methods for the Examination of Water and  Wastewater, 18th edition (1992), 19th edition (1995), or 20th edition (1998), American Public Health  Association   (APHA);   any   of these three editions may be  used. Method 6610 shall be followed in ac- cordance with Standard Methods for the Examination of Water and Wastewater, (18th Edition Supplement) (1994), or with the 19th edition (1995) or 20th edi- tion (1998) of Standard Methods for the Examination   of   Water   and   Wastewater;

#### Environmental Protection Agency	§ 141.24

any of these publications may be used. The  APHA   documents   are   available from APHA, 1015 Fifteenth Street NW., Washington, DC 20005. Other required analytical test  procedures  germane  to the conduct of these analyses are  con- tained in Technical  Notes  on  Drinking Water Methods, EPA/600/R–94–173, Octo- ber 1994, NTIS PB95–104766. EPA Meth-

ods  515.3  and  549.2  are  available  from

U.S. Environmental Protection  Agen- cy, National Exposure Research Lab- oratory (NERL)–Cincinnati, 26 West Martin Luther King Drive, Cincinnati, OH 45268. ASTM Method D 5317–93, 98 (Reapproved 2003) is available in the Annual Book of ASTM Standards, (1999), Vol. 11.02, ASTM International, 100 Barr	Harbor	Drive,	West Conshohocken, PA 19428, any edition containing the cited version of the method may be used. EPA Method 515.4, ‘‘Determination of Chlorinated Acids in Drinking Water by Liquid-Liq- uid   Microextraction,   Derivatization and   Fast   Gas   Chromatography   with

Electron    Capture    Detection,’’    Revision 1.0, April 2000, EPA/815/B–00/001 and EPA   Method   552.3,   ‘‘Determination   of Haloacetic	Acids	and		Dalapon	in Drinking	Water	by	Liquid-Liquid Microextraction,       Derivatization,       and Gas     Chromatography     with     Electron Capture   Detection,’’   Revision   1.0,   July 2003, EPA 815–B–03–002, can be accessed and     downloaded     directly     .  Syngenta  Method  AG–625, ‘‘Atrazine	in	Drinking		Water	by Immunoassay,’’  February  2001,  is  avail- able    from    Syngenta    Crop    Protection, Inc.,  410  Swing  Road,  P.O.  Box  18300, Greensboro,  NC  27419.  Telephone:  336–

632–6000. Method 531.2 ‘‘Measurement of N-methylcarbamoyloximes and N- methylcarbamates in Water by Direct Aqueous Injection  HPLC  with Postcolumn   Derivatization,’’   Revision 1.0, September 2001, EPA 815–B–01–002,

can be accessed and downloaded di- rectly online.

| Contaminant | EPA method | Standard methods | ASTM | Other |
| --- | --- | --- | --- | --- |
| 1. Benzene .............................................. | 502.2, 524.2. | ........................ | D5317–93, | Syngenta 5 |
| 2. Carbon tetrachloride ............................ | 502.2, 524.2, 551.1. |  |  |  |
| 3. Chlorobenzene .................................... | 502.2, 524.2. |  |  |  |
| 4. 1,2-Dichlorobenzene ........................... | 502.2, 524.2. |  |  |  |
| 5. 1,4-Dichlorobenzene ........................... | 502.2, 524.2. |  |  |  |
| 6. 1,2-Dichloroethane .............................. | 502.2, 524.2. |  |  |  |
| 7. cis-Dichloroethylene ............................ | 502.2, 524.2. |  |  |  |
| 8. trans-Dichloroethylene ........................ | 502.2, 524.2. |  |  |  |
| 9. Dichloromethane ................................. | 502.2, 524.2. |  |  |  |
| 10. 1,2-Dichloropropane .......................... | 502.2, 524.2. |  |  |  |
| 11. Ethylbenzene ..................................... | 502.2, 524.2. |  |  |  |
| 12. Styrene .............................................. | 502.2, 524.2. |  |  |  |
| 13. Tetrachloroethylene ........................... | 502.2, 524.2, 551.1. |  |  |  |
| 14. 1,1,1-Trichloroethane ........................ | 502.2, 524.2, 551.1. |  |  |  |
| 15. Trichloroethylene ............................... | 502.2, 524.2, 551.1. |  |  |  |
| 16. Toluene ............................................. | 502.2, 524.2. |  |  |  |
| 17. 1,2,4-Trichlorobenzene ..................... | 502.2, 524.2. |  |  |  |
| 18. 1,1-Dichloroethylene ......................... | 502.2, 524.2. |  |  |  |
| 19. 1,1,2-Trichloroethane ........................ | 502.2, 524.2, 551.1. |  |  |  |
| 20. Vinyl chloride ..................................... | 502.2, 524.2. |  |  |  |
| 21. Xylenes (total) ................................... | 502.2, 524.2. |  |  |  |
| 22. 2,3,7,8-TCDD (dioxin) ....................... | 1613. |  |  |  |
| 23. 2,4–D 4 (as acids, salts, and esters) | 515.2, 555, 515.1, 515.3, 515.4 .............. |  |  |  |
|  |  |  | 98 (Re- |  |
|  |  |  | ap- |  |
|  |  |  | proved |  |
|  |  |  | 2003). |  |
| 24. 2,4,5–TP 4 (Silvex) ............................ | 515.2, 555, 515.1, 515.3, 515.4 .............. | ........................ | D5317–93, |  |
|  |  |  | 98 (Re- |  |
|  |  |  | ap- |  |
|  |  |  | proved |  |
|  |  |  | 2003). |  |
| 25. Alachlor 2 ........................................... | 507, 525.2, 508.1, 505, 551.1. |  |  |  |
| 26. Atrazine 2 ........................................... | 507, 525.2, 508.1, 505, 551.1 ................. | ........................ | .................. |  |
|  |  |  |  | AG–625 |
| 27. Benzo(a)pyrene ................................. | 525.2, 550, 550.1. |  |  |  |
| 28. Carbofuran ........................................ | 531.1, 531.2 ............................................ | 6610. |  |  |
| 29. Chlordane .......................................... | 508, 525.2, 508.1, 505. |  |  |  |
| 30. Dalapon ............................................. | 552.1 515.1, 552.2, 515.3, 515.4, 552.3. |  |  |  |

#### § 141.24

40 CFR Ch. I (7–1–17 Edition)

| Contaminant | EPA method | Standard methods | ASTM | Other |
| --- | --- | --- | --- | --- |
| 31. Di(2-ethylhexyl)adipate ...................... | 506, 525.2. | 6651. | D5317–93, |  |
| 32. Di(2-ethylhexyl)phthalate ................... | 506, 525.2. |  |  |  |
| 33. Dibromochloropropane (DBCP) ........ | 504.1, 551.1. |  |  |  |
| 34. Dinoseb 4 ........................................... | 515.2, 555, 515.1, 515.3, 515.4. |  |  |  |
| 35. Diquat ................................................ | 549.2. |  |  |  |
| 36. Endothall ........................................... | 548.1. |  |  |  |
| 37. Endrin ................................................ | 508, 525.2, 508.1, 505, 551.1. |  |  |  |
| 38. Ethylene dibromide (EDB) ................ | 504.1, 551.1. |  |  |  |
| 39. Glyphosate ........................................ | 547 ........................................................... |  |  |  |
| 40. Heptachlor ......................................... | 508, 525.2, 508.1, 505, 551.1. |  |  |  |
| 41. Heptachlor Epoxide ........................... | 508, 525.2, 508.1, 505, 551.1. |  |  |  |
| 42. Hexachlorobenzene .......................... | 508, 525.2, 508.1, 505, 551.1. |  |  |  |
| 43. Hexachlorocyclopentadiene .............. | 508, 525.2, 508.1, 505, 551.1. |  |  |  |
| 44. Lindane .............................................. | 508, 525.2, 508.1, 505, 551.1. |  |  |  |
| 45. Methoxychlor ..................................... | 508, 525.2, 508.1, 505, 551.1. |  |  |  |
| 46. Oxamyl .............................................. | 531.1, 531.2 ............................................ | 6610. |  |  |
| 47. PCBs 3 (as decachlorobiphenyl) ....... | 508A. |  |  |  |
| 48. PCBs 3 (as Aroclors) ......................... | 508.1, 508, 525.2, 505. |  |  |  |
| 49. Pentachlorophenol ............................ | 515.2, 525.2, 555, 515.1, 515.3, 515.4 ... | ........................ |  |  |
|  |  |  | 98 (Re- |  |
|  |  |  | ap- |  |
|  |  |  | proved |  |
|  |  |  | 2003). |  |
| 50. Picloram 4 .......................................... | 515.2, 555, 515.1, 515.3, 515.4 .............. | ........................ | D5317–93, |  |
|  |  |  | 98 (Re- |  |
|  |  |  | ap- |  |
|  |  |  | proved |  |
|  |  |  | 2003). |  |
| 51. Simazine 2 ......................................... | 507, 525.2, 508.1, 505, 551.1. |  |  |  |
| 52. Toxaphene ........................................ | 508, 508.1, 525.2, 505. |  |  |  |
| 53. Total Trihalomethanes ...................... | 502.2, 524.2, 551.1. |  |  |  |

1 [Reserved]

2 Substitution of the detector specified in Method 505, 507, 508 or 508.1 for the purpose of achieving lower detection limits is allowed as follows. Either an electron capture or nitrogen phosphorous detector may be used provided all regulatory require- ments and quality control criteria are met.

3 PCBs are qualitatively identified as Aroclors and measured for compliance purposes as decachlorobiphenyl. Users of Method 505 may have more difficulty in achieving the required detection limits than users of Methods 508.1, 525.2 or 508.

4 Accurate determination of the chlorinated esters requires hydrolysis of the sample as described in EPA Methods 515.1, 515.2, 515.3, 515.4 and 555 and ASTM Method D5317–93.

5 This method may not be used for the analysis of atrazine in any system where chlorine dioxide is used for drinking water treatment. In samples from all other systems, any result for atrazine generated by Method AG–625 that is greater than one-half the maximum contaminant level (MCL) (in other words, greater than 0.0015mg/L or 1.5 g/L) must be confirmed using another approved method for this contaminant and should use additional volume of the original sample collected for compliance moni- toring. In instances where a result from Method AG–625 triggers such confirmatory testing, the confirmatory result is to be used to determine compliance.

- [Reserved]

- Beginning with the initial compli- ance period, analysis of the contami- nants  listed  in  § 141.61(a)  (1)  through

- for the purpose of determining compliance with the maximum con- taminant level shall be conducted as follows:

  - Groundwater systems shall take a minimum of one sample at every entry point to the distribution system which is representative of each well after treatment (hereafter called a sampling point). Each sample must be taken  at the same sampling point unless condi- tions make another sampling point more representative of each source, treatment plant, or within the dis- tribution  system.

  - Surface water  systems  (or  com- bined surface/ground) shall take a min- imum of one sample at points in the distribution system that are represent- ative of each source or at each entry point to the distribution system after treatment (hereafter called a sampling point). Each sample must be taken at the same sampling point unless condi- tions make another sampling point more representative of each source, treatment plant, or within the dis- tribution system.

  - If the system draws water from more than one source and the sources are combined before distribution, the system must sample at an entry point to the distribution system during peri- ods   of   normal   operating   conditions

#### Environmental Protection Agency	§ 141.24

(i.e., when water representative of all sources is being used).

  - Each community and non-tran- sient non-community water system shall take four consecutive quarterly samples for each contaminant listed in

§ 141.61(a) (2) through (21) during each compliance period, beginning  in  the initial   compliance   period.

  - If the initial monitoring for con- taminants listed in § 141.61(a)  (1) through (8) and the monitoring for the contaminants listed in § 141.61(a) (9) through (21) as allowed in paragraph (f)(18) has been completed by December 31, 1992, and the system did not detect any contaminant listed in § 141.61(a) (1) through (21), then each ground and sur- face water system shall take one  sam- ple annually beginning with the initial compliance   period.

  - After a minimum of three years of annual sampling, the State may allow groundwater systems with no previous detection of any contaiminant listed in

§ 141.61(a) to take one sample during each  compliance  period.

  - Each community and non-tran- sient non-community ground water system which does not detect a con- taminant listed in § 141.61(a)  (1) through (21) may apply to the State for a waiver from the requirements of paragraphs (f)(5) and (f)(6) of this sec- tion after completing the initial moni- toring. (For purposes of this section, detection is defined as 0.0005 mg/l.) A waiver shall be effective for no more than six years (two  compliance  peri- ods). States may also issue waivers to small systems for the initial round of monitoring  for  1,2,4-trichlorobenzene.

  - A State may grant a waiver after evaluating the following factor(s):

    - Knowledge of previous use (includ- ing transport, storage, or disposal) of the contaminant within the watershed or zone of influence of the system. If a determination by the State reveals no previous use of the contaminant within the watershed or zone of influence, a waiver may be granted.

    - If previous use of the contami- nant is unknown or it has been used previously, then the following factors shall be used to determine whether a waiver is granted.

      - Previous analytical  results.

      - The proximity of the system to a potential point or non-point source of contamination. Point sources include spills and leaks of chemicals at or near a water treatment facility or at manu- facturing, distribution, or storage fa- cilities, or from hazardous and munic- ipal waste landfills and other waste handling or treatment facilities.

      - The environmental persistence and transport of the contaminants.

      - The number of persons served by the public water system and the prox- imity of a smaller system to a larger system.

      - How well the water source is pro- tected against contamination, such as whether it is a surface or groundwater system. Groundwater systems must consider factors such as depth of the well, the type of soil, and wellhead pro- tection. Surface water systems must consider watershed protection.

  - As a condition of the waiver a groundwater system must take one sample at each sampling point during the time the waiver is effective (i.e., one sample during two compliance pe- riods or six years) and update its vul- nerability assessment considering the factors listed in paragraph (f)(8) of this section. Based on this vulnerability as- sessment the  State  must   reconfirm that the system is non-vulnerable. If the State does not make this recon- firmation within three years of the ini- tial determination, then the waiver is invalidated and the system is required to sample annually as specified in paragraph (5) of this section.

  - Each community and non-tran- sient non-community surface water system which does not detect a con- taminant listed  in § 141.61(a) (1) through (21) may apply to the State for a waiver from the requirements of (f)(5) of this section after completing the ini- tial monitoring. Composite  samples from a maximum of five sampling points are allowed, provided that the detection limit  of the  method used for analysis is less than one-fifth of the MCL. Systems meeting this criterion must be determined by the State to be non-vulnerable based on a  vulner- ability assessment  during  each compli- ance period. Each system receiving a waiver shall sample at the frequency specified by the State (if any).

#### § 141.24

  - If    a    contaminant    listed    in

§ 141.61(a) (2) through (21) is detected at a level  exceeding 0.0005  mg/l  in any sample,   then:

- The system must monitor quar- terly at each sampling point which re- sulted in a detection.

- The State may decrease the quar- terly monitoring requirement speci fied in paragraph (f)(11)(i) of this sec- tion provided it has determined that the system is reliably and consistently below the maximum contaminant level. In no case shall the State make this determination unless a ground- water system takes a minimum of two quarterly samples and a surface water system takes a minimum of four quar- terly samples.

- If the State determines that the system is reliably and consistently below the MCL, the State may  allow the system to monitor annually. Sys- tems which monitor annually must monitor during the quarter(s) which previously yielded the highest analyt- ical result.

- Systems which  have  three con- secutive annual samples with no detec- tion of a contaminant may apply to the State for a waiver as specified in para- graph (f)(7) of this section.

- Groundwater systems which have detected one or more of the following two-carbon organic compounds: tri- chloroethylene, tetrachloroethylene, 1,2-dichloroethane,	1,1,1-trichloro- ethane, cis-1,2-dichloroethylene, trans- 1,2-dichloroethylene,		or	1,1- dichloroethylene shall monitor quar- terly for vinyl chloride. A vinyl chlo- ride sample shall be taken at each sam- pling point at which one or more of the two-carbon organic compounds was de- tected. If the results of the first anal- ysis do not detect vinyl chloride, the State may reduce the quarterly moni- toring frequency of vinyl chloride mon- itoring to one sample during each com- pliance period. Surface water systems are required to monitor for vinyl chlo- ride as specified by the State.

  - Systems which violate the re- quirements of § 141.61(a) (1) through (21), as determined by paragraph (f)(15) of  this  section,  must  monitor   quar- terly. After a minimum of four con- secutive quarterly samples which show the  system  is  in  compliance  as  speci-

#### 40 CFR Ch. I (7–1–17 Edition)

fied in paragraph (f)(15) of this section the system and the State determines that the system is reliably and consist- ently below the maximum contaminant level, the system may monitor at the frequency and times specified in para- graph (f)(11)(iii) of this section.

  - The State may require a con- firmation sample for positive or nega- tive results. If a confirmation sample is required by the State, the result must be averaged with the first sampling re- sult and the average is used for the compliance determination as specified by paragraph (f)(15). States have discre- tion to delete results of obvious sam- pling errors from this calculation.

  - The State may reduce the total number of samples a system must ana- lyze by allowing the use  of compositing. Composite  samples  from a maximum of five sampling points are allowed, provided that the detection limit of the method used for analysis is less than one-fifth of the MCL. Compositing of samples must  be  done in the laboratory and analyzed  within 14 days of sample collection.

- If the concentration in the com- posite sample is greater  than  or  equal to 0.0005 mg/l for any contaminant list- ed in § 141.61(a), then a follow-up  sam- ple must  be  taken within  14  days at each sampling point included in the composite, and be analyzed for that contaminant.

- If duplicates of the original sam- ple taken from each  sampling  point used in the composite sample are avail- able, the system may use these instead of resampling. The duplicates must be analyzed and the results reported to the State within 14 days after com- pleting analysis of the composite sam- ple, provided the holding time of the sample is not exceeded.

- If the population served by the system is >3,300 persons, then compositing may only be permitted by the State at sampling points within a single system. In systems serving 3,300 persons, the State may permit compositing among different systems provided the 5-sample limit is main- tained.

- Compositing samples prior to GC analysis.

#### Environmental Protection Agency	§ 141.24

  - Add 5 ml or equal larger amounts of each sample (up to 5 samples are al- lowed) to a 25 ml glass syringe. Special precautions must be made to maintain zero headspace in the syringe.

  - The samples must be cooled at 4

C during this step to minimize vola- tilization losses.

  - Mix well and draw out a 5-ml ali- quot for analysis.

  - Follow sample introduction, purging, and desorption steps described in the method.

  - If less than five samples are used for compositing, a proportionately small syringe may be used.

- Compositing samples prior to GC/ MS analysis.

- Inject 5-ml or equal larger amounts of each aqueous sample (up to

5 samples are allowed) into a 25-ml purging device using the sample intro- duction technique described in the method.

- The total volume of the sample in the purging device must be 25 ml.

- Purge and desorb as described in the method.

  - Compliance with § 141.61(a) (1) through (21) shall be determined based on the  analytical results obtained  at each sampling point. If one sampling point is in violation of an MCL, the system is in violation of the MCL.

- For systems monitoring more than once per year, compliance with the MCL is determined by a running annual average at each sampling point.

- Systems monitoring annually  or less frequently whose sample result ex- ceeds the MCL must begin quarterly sampling. The system will not be con- sidered in violation of the MCL until it has completed one year of quarterly sampling.

- If any sample result will cause the running annual average to exceed the MCL at any sampling point, the system is out of compliance with the MCL  immediately.

- If a system fails to collect the re- quired number of samples, compliance will be based on the total number of samples  collected.

- If a sample result is less than the detection limit, zero will be used to calculate the annual average.

  - [Reserved]

  - Analysis under this section shall only be conducted by laboratories that are certified by EPA or the State ac- cording to the following conditions (laboratories may conduct sample analysis under provisional certification until January 1, 1996):

- To receive certification to conduct analyses    for    the    contaminants    in

§ 141.61(a)  (2)  through  (21)  the  labora- tory    must:

- Analyze Performance Evaluation (PE) samples provided by EPA, the State, or by a third party (with the ap- proval of the State or EPA) at least once a year by each method for which the laboratory desires certification.

- Achieve the quantitative accept- ance limits under paragraphs (f)(17)(i)(C) and (D) of this section for at least 80 percent of the regulated or- ganic contaminants included in the PE sample.

- Achieve  quantitative  results   on the analyses performed under  para- graph (f)(17)(i)(A) of this section that are within 20% of  the  actual  amount of the substances in the Performance Evaluation sample when the actual amount is greater than or equal to 0.010 mg/l.

- Achieve  quantitative  results   on the analyses performed under  para- graph (f)(17)(i)(A) of this section that are within 40 percent of the actual amount of the  substances in  the Per- formance Evaluation sample when the actual amount is less than 0.010 mg/l.

- Achieve a method detection  limit of 0.0005 mg/l, according to the proce- dures in appendix B of part 136.

- To receive certification to con- duct analyses for vinyl chloride, the laboratory must:

  - Analyze Performance Evaluation (PE) samples provided by EPA, the State, or by a third party (with the ap- proval of the State or EPA) at least once a year by each method for which the laboratory desires certification.

  - Achieve quantitative results  on the analyses performed under para- graph (f)(17)(ii)(A) of this section that are within 40 percent of the actual amount of vinyl chloride in the Per- formance  Evaluation  sample.

  - Achieve a method detection  limit of 0.0005 mg/l, according to the proce- dures in appendix B of part 136.

#### § 141.24

  - Obtain certification for the con- taminants listed in § 141.61(a)(2) through (21).

  - States may allow the use of mon- itoring data collected after January 1, 1988, required under section 1445 of the Act for purposes of initial monitoring compliance. If the data are generally consistent with the  other  requirements of this section, the State may use these data (i.e., a single sample rather than four quarterly samples) to satisfy the initial monitoring requirement of para- graph (f)(4) of this section. Systems which use grandfathered  samples  and did   not   detect   any   contaminant   listed

§ 141.61(a)(2) through (21) shall begin monitoring   annually   in    accordance with paragraph (f)(5) of this section be- ginning with the initial compliance pe- riod.

  - States may increase required monitoring where necessary to detect variations within the system.

  - Each certified laboratory must determine the method detection limit (MDL), as defined in appendix B to part 136, at which it is capable of detecting VOCs. The acceptable MDL is 0.0005 mg/l. This concentration  is  the  detec- tion concentration for purposes of this section.

  - Each public water system shall monitor at the time designated by the State within each compliance period.

  - All new systems or systems that use a new source of water that begin operation after January 22, 2004 must demonstrate compliance with the MCL within a period of time specified by the State. The system must  also  comply with the initial sampling frequencies specified by the State to ensure a sys- tem can demonstrate compliance with the MCL. Routine and increased moni- toring frequencies shall be  conducted in accordance with the requirements in this  section.

- [Reserved]

- Analysis of the contaminants list- ed in § 141.61(c) for the purposes of de- termining compliance with the max- imum contaminant level shall be con- ducted as follows, with the exception that no monitoring is required for aldicarb, aldicarb sulfoxide or aldicarb sulfone:

  - Groundwater systems shall take a minimum of one sample at every entry

#### 40 CFR Ch. I (7–1–17 Edition)

point to the distribution system which is representative of each well after treatment (hereafter called a sampling point). Each sample must be taken  at the same sampling point unless condi- tions make another sampling point more representative of each source or treatment   plant.

  - Surface water  systems  shall  take a minimum of one sample at points in the distribution system that are rep- resentative of each source or at each entry point to the distribution system after treatment (hereafter called a sampling point). Each sample must be taken at the same sampling point un- less conditions make another sampling point more representative of each source or treatment plant.

NOTE: For purposes of this paragraph, sur- face water systems include systems with a combination of surface and ground sources.

  - If the system draws water from more than one source and the sources are combined before distribution, the system must sample at  an  entry  point to the distribution system during peri- ods of normal operating  conditions (i.e., when water representative of all sources is being used).

  - Monitoring frequency: (i) Each community and non-transient non- community water system shall  take four consecutive quarterly samples for each contaminant listed in § 141.61(c) during each compliance period begin- ning with the initial  compliance  pe- riod.

- Systems serving more than 3,300 persons which do not detect a contami- nant in the initial compliance period may reduce  the  sampling  frequency  to a minimum of two quarterly samples in one year during each repeat compli- ance period.

- Systems serving less than or equal to 3,300 persons which do not de- tect a contaminant in the initial com- pliance period may reduce the  sam- pling frequency to a minimum of one sample during each repeat compliance period.

  - Each community and non-tran- sient water system may apply to the State for a waiver from the require- ment of paragraph (h)(4) of this sec- tion. A system must reapply for a waiver for each compliance period.

#### Environmental Protection Agency	§ 141.24

  - A State may grant a waiver after evaluating the following factor(s): Knowledge of previous use (including transport, storage, or disposal) of the contaminant within the watershed or zone of influence of the system. If a de- termination by the State reveals no previous use of the contaminant within the watershed or zone of influence, a waiver may be granted. If previous use of the contaminant is unknown or it has been used previously, then the fol- lowing factors shall be used to deter- mine whether a waiver is granted.

    - Previous analytical results.

    - The proximity of the system to a potential point or non-point source of contamination. Point sources include spills and leaks of chemicals at or near a water treatment facility or at manu- facturing, distribution, or storage fa- cilities, or from hazardous and munic- ipal waste landfills and other waste handling or treatment facilities. Non- point sources include the use of pes- ticides to control insect and weed pests on agricultural areas, forest lands, home and gardens, and other land ap- plication uses.

    - The environmental persistence and transport of the pesticide or PCBs.

    - How well the water source is pro- tected against contamination due to such factors as depth of the well and the type of soil and the integrity of the well casing.

    - Elevated nitrate levels at the water supply source.

    - Use of PCBs in equipment used in the production, storage, or distribution of water (i.e., PCBs used in pumps, transformers, etc.).

  - If  an  organic  contaminant   listed in § 141.61(c) is detected (as defined by paragraph (h)(18) of this section) in any sample,   then:

    - Each system must monitor quar- terly at each sampling point which re- sulted in a detection.

    - The State may decrease the quar- terly monitoring requirement specified in paragraph (h)(7)(i) of this section provided it has determined that the system is reliably and consistently below the maximum contaminant level. In no case shall the State make this determination unless a ground- water system takes a minimum of two quarterly samples and a surface water

system takes a minimum of four quar- terly samples.

    - After the State determines the system is reliably and consistently below the maximum contaminant level the State may allow the system to monitor annually. Systems which mon- itor annually must monitor during the quarter that previously yielded the highest analytical result.

    - Systems which have 3  consecu- tive annual samples with  no  detection of a contaminant may  apply  to  the State for a waiver as specified in para- graph (h)(6) of this section.

    - If the monitoring results in detec- tion of one or more of certain related contaminants (heptachlor and hepta- chlor epoxide), then subsequent moni- toring shall analyze for all related con- taminants.

  - Systems which violate the re- quirements of § 141.61(c) as determined by paragraph (h)(11) of this  section must monitor quarterly. After a min- imum of four quarterly samples show the system is in  compliance  and  the State determines the system is reliably and consistently below the MCL, as specified in paragraph (h)(11) of this section,  the  system  shall  monitor  at the frequency specified in paragraph (h)(7)(iii) of this section.

  - The State may require a con- firmation sample for positive or nega- tive results. If a confirmation sample is required by the State, the result must be averaged with the first sampling re- sult and the average used for the com- pliance determination as specified by paragraph (h)(11) of this section. States have discretion to delete results of ob- vious sampling errors from this cal- culation.

  - The State may reduce the total number of samples a system must ana- lyze by allowing the use  of compositing. Composite  samples  from a maximum of five sampling points are allowed, provided that the detection limit of the method used for analysis is less than one-fifth of the MCL. Compositing of samples must  be  done in the laboratory and analyzed  within 14 days of sample collection.

- If the concentration in the com- posite sample detects one or more con- taminants listed in § 141.61(c), then a follow-up sample must be taken within

#### § 141.24

14 days at each sampling point included in the composite, and be analyzed for that   contaminant.

- If duplicates of the original sam- ple taken from each  sampling  point used in the composite sample are avail- able, the system may use these instead of resampling. The duplicates must be analyzed and the results reported to the State within 14 days after comple- tion of the composite analysis or before the holding time  for  the  initial  sample is exceeded whichever is sooner.

- If the population served by the system is >3,300 persons, then compositing may only be permitted by the State at sampling points within a single system. In systems serving 3,300 persons, the State may permit compositing among different systems provided the 5-sample limit is main- tained.

  - Compliance with § 141.61(c) shall be determined based on the analytical results obtained at each  sampling point. If one sampling point is in viola- tion of an MCL, the system is in viola- tion of the MCL.

    - For systems monitoring more than once per year, compliance with the MCL is determined by a running annual average at each sampling point.

    - Systems monitoring annually or less frequently whose sample result ex- ceeds the regulatory detection level as defined by paragraph (h)(18) of this sec- tion must begin quarterly  sampling. The system will not be considered in violation of the MCL until it has com- pleted  one  year  of  quarterly  sampling.

    - If any sample result will cause the running annual average to exceed the MCL at any sampling point, the system is out of compliance with the MCL  immediately.

    - If a system fails to collect the re- quired number of samples, compliance will be based on the total number of samples  collected.

    - If a sample result is less than the detection limit, zero will be used to calculate the annual average.

  - [Reserved]

  - Analysis for PCBs shall be con- ducted as follows using the methods in paragraph (e) of this section:

- Each system which monitors for PCBs shall analyze each sample using either Method  508.1, 525.2, 508  or 505.

#### 40 CFR Ch. I (7–1–17 Edition)

Users of Method 505 may have more dif- ficulty in achieving  the  required Aroclor detection limits than users of Methods 508.1, 525.2 or 508.

- If PCBs (as one of seven Aroclors) are detected (as designated in this paragraph) in any sample analyzed using Method 505 or 508, the system shall reanalyze the sample using Meth- od 508A to quantitate PCBs (as decachlorobiphenyl).

| Aroclor | Detection limit (mg/ l) |
| --- | --- |
| 1016 ....................................................... | 0.00008 |
| 1221 ....................................................... | 0.02 |
| 1232 ....................................................... | 0.0005 |
| 1242 ....................................................... | 0.0003 |
| 1248 ....................................................... | 0.0001 |
| 1254 ....................................................... | 0.0001 |
| 1260 ....................................................... | 0.0002 |

- Compliance with the PCB MCL shall be determined based upon the quantitative results of analyses using Method 508A.

  - If monitoring data collected after January 1, 1990, are generally con- sistent     with     the     requirements     of

§ 141.24(h), then the State may allow systems to use that data to satisfy the monitoring requirement for the initial compliance  period  beginning   January 1, 1993.

  - The State may increase the re- quired monitoring frequency, where necessary, to detect variations within the system (e.g., fluctuations in con- centration due to seasonal use, changes in water source).

  - The State has the authority to determine compliance or initiate en- forcement action based upon analytical results and other information compiled by their sanctioned representatives and agencies.

  - Each public water system shall monitor at the time designated by the State within each compliance period.

  - Contaminant

Detection limit (mg/l)

Alachlor 	0002

Aldicarb	0005

Aldicarb sulfoxide	0005

Aldicarb sulfone	0008

Atrazine	0001

Benzo[a]pyrene	00002

Carbofuran	0009

Detection as used in this para- graph shall be defined as greater than or equal to the following concentra- tions for each contaminant.

| Contaminant | Detection limit (mg/l) |
| --- | --- |
| Chlordane ........................................................ | .0002 |
| Dalapon ........................................................... | .001 |
| 1,2–Dibromo–3–chloropropane (DBCP) .......... | .00002 |
| Di (2-ethylhexyl) adipate .................................. | .0006 |
| Di (2-ethylhexyl) phthalate ............................... | .0006 |
| Dinoseb ............................................................ | .0002 |
| Diquat .............................................................. | .0004 |
| 2,4-D ................................................................ | .0001 |
| Endothall .......................................................... | .009 |
| Endrin .............................................................. | .00001 |
| Ethylene dibromide (EDB) ............................... | .00001 |
| Glyphosate ....................................................... | .006 |
| Heptachlor ....................................................... | .00004 |
| Heptachlor epoxide .......................................... | .00002 |
| Hexachlorobenzene ......................................... | .0001 |
| Hexachlorocyclopentadiene ............................. | .0001 |
| Lindane ............................................................ | .00002 |
| Methoxychlor ................................................... | .0001 |
| Oxamyl ............................................................. | .002 |
| Picloram ........................................................... | .0001 |
| Polychlorinated biphenyls (PCBs) (as |  |
| decachlorobiphenyl) ..................................... | .0001 |
| Pentachlorophenol ........................................... | .00004 |
| Simazine .......................................................... | .00007 |
| Toxaphene ....................................................... | .001 |
| 2,3,7,8-TCDD (Dioxin) ..................................... | .000000005 |
| 2,4,5-TP (Silvex) .............................................. | .0002 |

Environmental Protection Agency	§ 141.25

| Contaminant | Acceptance limits (percent) |
| --- | --- |
| Endothall ................................ | 2 standard deviations. |
| Endrin .................................... | 30. |
| Glyphosate ............................. | 2 standard deviations. |
| Heptachlor ............................. | 45. |
| Heptachlor epoxide ................ | 45. |
| Hexachlorobenzene ............... | 2 standard deviations. |
| Hexachloro- cyclopentadiene | 2 standard deviations. |
| Lindane .................................. | 45. |
| Methoxychlor ......................... | 45. |
| Oxamyl ................................... | 2 standard deviations. |
| PCBs (as | 0–200. |
| Decachlorobiphenyl) |  |
| Picloram ................................. | 2 standard deviations. |
| Simazine ................................ | 2 standard deviations. |
| Toxaphene ............................. | 45. |
| Aldicarb .................................. | 2 standard deviations. |
| Aldicarb sulfoxide .................. | 2 standard deviations. |
| Aldicarb sulfone ..................... | 2 standard deviations. |
| Pentachlorophenol ................. | 50. |
| 2,3,7,8-TCDD (Dioxin) ........... | 2 standard deviations. |
| 2,4-D ...................................... | 50. |
| 2,4,5-TP (Silvex) .................... | 50. |

  - Anaylsis under this section shall only be conducted by laboratories that have received certification by EPA or the State and have met the following conditions:

- To receive certification to conduct analyses    for    the    contaminants    in

§ 141.61(c)  the  laboratory  must:

- Analyze Performance Evaluation (PE) samples provided by EPA, the State, or by a third party (with the ap- proval of the State or EPA) at least once a year by each method for which the laboratory desires certification.

- Contaminant

Acceptance limits (percent)

DBCP .....................................   40

EDB  .......................................   40.

Alachlor ..................................   45.

Atrazine ..................................   45.

Benzo[a]pyrene ......................   2 standard deviations.

Carbofuran .............................   45.

Chlordane ..............................   45.

Dalapon ................................. 2 standard deviations. Di(2-ethylhexyl)adipate .......... 2 standard deviations. Di(2-ethylhexyl)phthalate ....... 2 standard deviations. Dinoseb ..................................   2 standard deviations.

Diquat  ....................................   2 standard deviations.

For each contaminant that has been included in the PE sample achieve quantitative results on the analyses that are within the following accept- ance limits:

- [Reserved]

  - All new systems or systems that use a new source of water that begin operation after January 22, 2004 must demonstrate compliance with the MCL within a period of time specified by the State. The system must  also  comply with the initial sampling frequencies specified by the State to ensure a sys- tem can demonstrate compliance with the MCL. Routine and increased moni- toring frequencies shall be  conducted in accordance with the requirements in this  section.

(Approved by the Office of Management and Budget under control number 2040–0090)

[40 FR 59570, Dec. 24, 1975]

EDITORIAL NOTE: For FEDERAL REGISTER ci-

tations affecting § 141.24, see the List of CFR Sections Affected, which appears in  the Finding Aids  section of  the printed volume

##### § 141.25   Analytical  methods  for  radio- activity.

- Analysis for the following con- taminants shall be conducted to deter- mine compliance with § 141.66 (radioac- tivity) in accordance with the methods in the following table, or the  alter- native methods listed in appendix A to subpart C this part, or their equivalent determined by EPA in accordance with

§ 141.27.

§ 141.25

40 CFR Ch. I (7–1–17 Edition)

426

| Contaminant | Methodology | Reference (Method of Page Number) |
| --- | --- | --- |
|  |  | EPA 1 | EPA 2 | EPA 3 | EPA 4 | SM 5 | ASTM 6 | USGS 7 | DOE 8 | Other |
| Naturally Occurring: | Evaporation .......... Coprecipitation ..... Radon emanation Radiochemical ..... Radiochemical ..... Radiochemical ..... Fluorometric ......... ICP–MS ............... Alpha Spectrom- etry. Laser Phosphorimetry. Radiochemical ..... Gamma Ray Spectrometry. Radiochemical ..... | 900.0 ................ 903.1 903.0 904.0 908.0 908.1 200.8 13 ................ ................ 901.0 901.1 902.0 | p. 1 ... .......... p. 16 p. 13 p. 24 .......... .......... .......... .......... .......... p. 4 ... .......... p. 6 ... | 00–01 00–02 Ra–04 Ra-03 Ra-05 ............ ............ ............ 00–07 ............ ............ ............ ............ | p. 1 ........ ............... p. 19 ...... ............... p. 19 ...... ............... ............... ............... p. 33 ...... ............... ............... p. 92 ...... ............... | 302, 7110 B, 7110 B–00. 7110 C, 7110 C–00. 305, 7500–Ra C, 7500– Ra C–01. 304, 7500–Ra B, 7500–Ra B–01. 7500–Ra D, 7500–Ra D–01. 7500–U B, 7500–U B– 00. 7500–U C (17th Ed.). 3125 ............. 7500–U C (18th, 19th, or 20th Ed.), 7500– U C–00. ...................... 7500–Cs B, 7500–Cs B–00. 7120, 7120– 97. 7500–I B, | ................ D3454–97 D2460–97 ................ D2907–97 D5673–03. D3972– 97, 02. D5174– 97, 02. D2459–72 D3649– 91, 98a. | R–1120–76. R–1141–76 R–1140–76 R–1142–76 R–1180–76, R–1181– 76. R–1182–76 R–1111–76. R–1110–76 | Ra-04 ..... ................ ................ U–04. U–02. 4.5.2.3. | NY 9, GA 14 NY 9, NJ 10, GA 14 |
| Gross alpha 11 and beta .. Gross alpha 11 ................. Radium 226 ..................... Radium 228 ..................... Uranium 12 ....................... Man-Made: Radioactive Cesium ........ Radioactive Iodine ........... |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  | 7500–I B– |  |  |  |  |
|  |  |  |  |  |  | 00. |  |  |  |  |
|  |  |  | p. 9 ... | ............ | ............... | 7500–I C, |  |  |  |  |
|  |  |  |  |  |  | 7500–I C– |  |  |  |  |
|  |  |  |  |  |  | 00. |  |  |  |  |

427

Gamma Ray

Spectrometry. Radiochemical .....

901.1    ..........    ............   p. 92 ......

7500–I D,

7500–I D–

00.

7120, 7120–

97.

303, 7500–Sr B, 7500–Sr B–01.

306, 7500–

3 H B,

7500–3 H B–00.

D3649–

91, 98a.

D4785–

93, 00a.

................

....................   4.5.2.3.

Radioactive Strontium 89,

90.

905.0

p. 29

Sr–04

p. 65 ......

R–1160–76

Sr–01,

Sr–02.

Tritium  .............................

Liquid Scintillation

906.0

p. 34

H–02 ..

p. 87 ......

D4107–

91, 98 (Re-

ap- proved 2002).

D3649– 91, 98a.

D4785– 93, 00a.

R–1171–76.

Gamma Emitters .............

Gamma Ray

Spectrometry.

901.1

..........

............

p. 92 ......

7120, 7120–

97.

7500–Cs B,

7500–Cs B–00.

7500–I B,

7500–I B–

00.

R–1110–76

Ga–01–R.

902.0

..........

............

...............

901.0

..........

............

...............

Environmental Protection Agency

The procedures shall be done in accordance with the documents listed below. The incorporation by reference of documents 1 through 10 and 13 through 14 was approved by the Di- rector of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies of the documents may be obtained from the sources listed below. Information regarding ob- taining these documents can be obtained from the Safe Drinking Water Hotline at 800–426–4791. Documents may be inspected at EPA’s Drinking Water Docket, EPA West, 1301 Con- stitution Avenue, NW., Room 3334 , Washington, DC 20460 (Telephone: 202–566–2426); or at the National Archives and Records Administration (NARA). For information on the avail- ability  of  this  material  at  NARA,  call  202–741–6030

1 ‘‘Prescribed Procedures for the Measurement of Radioactivity in Drinking Water,’’ EPA 600/4–80–032, August 1980. Available at the U.S. Department of Commerce, National Tech- nical Information Service (NTIS), 5285 Port Royal Road, Springfield, VA 22161 (Telephone 800–553–6847), PB 80–224744.

2 ‘‘Interim Radiochemical Methodology for Drinking Water,’’ EPA 600/4–75–008 (revised), March 1976. Available NTIS, ibid.

3 ‘‘Radiochemistry Procedures Manual,’’ EPA 520/5–84–006, December 1987. Available NTIS, ibid.

4 ‘‘Radiochemical Analytical Procedures for Analysis of Environmental Samples,’’ March 1979. Available at NTIS, ibid. EMSL LV 053917.

5 ‘‘Standard Methods for the Examination of Water and Wastewater,’’ 13th, 17th, 18th, 19th or 20th edition, 1971, 1989, 1992, 1995, 1998. Available at American Public Health Associa- tion, 1015 Fifteenth Street, NW., Washington, DC 20005. Methods 302, 303, 304, 305 and 306 are only in the 13th edition. Methods 7110B, 7500–Ra B, 7500–Ra C, 7500–Ra D, 7500– U B, 7500–Cs B, 7500–I B, 7500–I C, 7500–I D, 7500–Sr B, and 7500–3H B are in the 17th, 18th, 19th and 20th editions. Method 7110 C is in the 18th, 19th and 20th editions. Method 7500–U C Fluorometric Uranium is only in the 17th Edition, and 7500–U C Alpha spectrometry is only in the 18th, 19th and 20th editions. Method 7120 is only in the 19th and 20th edi- tions. Method 3125 is only in the 20th edition. Methods 7110 B–00, 7110 C–00, 7500–Ra B–01, 7500–Ra C–01, 7500–Ra D–01, 7500–U B–00, 7500–U C–00, 7500–I B–00, 7500–I C–

00, 7500–I D–00, 7120–97, 7500–Sr B–01, and 7500–3H B–00 are available online The year in which each method was approved by the Standard Methods Committee is designated by the last two digits in the method number. The methods listed are the only online versions that may be used.

6 Annual Book of ASTM Standards, Vol. 11.01 and 11.02, 2002; ASTM International; any year containing the cited version of the method may be used. Copies of these two volumes and the 2003 version of D 5673–03 may be obtained from ASTM International, 100 Barr Harbor Drive, P.O. Box C700, West Conshohocken, PA 19428–2959.

7 ‘‘Methods for Determination of Radioactive Substances in Water and Fluvial Sediments,’’ Chapter A5 in Book 5 of Techniques of Water-Resources Investigations of the United States Geological Survey, 1977. Available at U.S. Geological Survey (USGS) Information Services, Box 25286, Federal Center, Denver, CO 80225–0425.

§ 141.25

8 ‘‘EML Procedures Manual,’’ 28th (1997) or 27th (1990) Editions, Volumes 1 and 2; either edition may be used. In the 27th Edition Method Ra-04 is listed as Ra-05 and Method Ga- 01–R is listed as Sect. 4.5.2.3. Available at the Environmental Measurements Laboratory, U.S. Department of Energy (DOE), 376 Hudson Street, New York, NY 10014–3621.

9 ‘‘Determination of Ra–226 and Ra–228 (Ra–02),’’ January 1980, Revised June 1982. Available at Radiological Sciences Institute for Laboratories and Research, New York State De- partment of Health, Empire State Plaza, Albany, NY 12201.

10 ‘‘Determination of Radium 228 in Drinking Water,’’ August 1980. Available at State of New Jersey, Department of Environmental Protection, Division of Environmental Quality, Bureau of Radiation and Inorganic Analytical Services, 9 Ewing Street, Trenton, NJ 08625.

40 CFR Ch. I (7–1–17 Edition)

428

§ 141.25

11 Natural uranium and thorium-230 are approved as gross alpha calibration standards for gross alpha with co-precipitation and evaporation methods; americium-241 is approved with co-precipitation methods.

12 If uranium (U) is determined by mass, a 0.67 pCi/g of uranium conversion factor must be used. This conversion factor is based on the 1:1 activity ratio of U–234 and U–238 that is characteristic of naturally occurring uranium.

13 ‘‘Determination of Trace Elements in Waters and Wastes by Inductively Coupled Plasma-Mass Spectrometry,’’ Revision 5.4, which is published in ‘‘Methods for the Determination of Metals in Environmental Samples—Supplement I,’’ ’ EPA 600–R–94–111, May 1994. Available at NTIS, PB 95–125472.

14 ‘‘The Determination of Radium-226 and Radium-228 in Drinking Water by Gamma-ray Spectrometry Using HPGE or Ge(Li) Detectors,’’ Revision 1.2, December 2004. Available from the Environmental Resources Center, Georgia Institute of Technology, 620 Cherry Street, Atlanta, GA 30332–0335, USA, Telephone: 404–894–3776. This method may be used to ana- lyze for radium-226 and radium-228 in samples collected after January 1, 2005 to satisfy the radium-226 and radium-228 monitoring requirements specified at 40 CFR 141.26.

#### Environmental Protection Agency	§ 141.26

- When the identification and meas- urement of radionuclides  other  than those listed in paragraph (a) of this section is required, the following ref- erences are to be used, except in cases where alternative methods have been approved in accordance with § 141.27.

  - Procedures for Radiochemical Anal- ysis of Nuclear Reactor Aqueous Solu- tions, H. L. Krieger and S. Gold, EPA- R4–73–014. USEPA, Cincinnati, Ohio, May 1973.

  - HASL Procedure Manual, Edited by John H. Harley.  HASL  300,  ERDA Health and Safety Laboratory, New York, NY., 1973.

- For the purpose of monitoring ra- dioactivity concentrations in drinking water, the required sensitivity of the radioanalysis is defined in terms of a detection  limit.  The  detection  limit shall be that concentration which  can be counted with a precision of plus or minus 100 percent at the 95 percent confidence level (1.96s where s is the standard deviation  of  the net counting rate of the sample).

- To  determine  compliance  with

§ 141.66(b), (c), and (e) the detection limit shall not exceed the concentra- tions in Table B to this paragraph.

TABLE B—DETECTION LIMITS FOR GROSS ALPHA PARTICLE ACTIVITY, RADIUM 226, RADIUM 228, AND URANIUM

| Contaminant | Detection limit |
| --- | --- |
| Gross alpha particle activity .......................... | 3 pCi/L. |
| Radium 226 ................................................... | 1 pCi/L. |
| Radium 228 ................................................... | 1 pCi/L. |
| Uranium ......................................................... | 1 g/L |

- To  determine  compliance  with

§ 141.66(d) the detection limits shall not exceed the concentrations  listed  in Table  C  to  this  paragraph.

TABLE C—DETECTION LIMITS FOR MAN-MADE BETA PARTICLE AND PHOTON EMITTERS

| Radionuclide | Detection limit |
| --- | --- |
| Tritium .................................... | 1,000 pCi/1. |
| Strontium–89 ......................... | 10 pCi/1. |
| Strontium–90 ......................... | 2 pCi/1. |
| Iodine–131 ............................. | 1 pCi/1. |
| Cesium–134 ........................... | 10 pCi/1. |
| Gross beta ............................. | 4 pCi/1. |
| Other radionuclides ............... | 1⁄10 of the applicable limit. |

- To judge compliance with the maximum contaminant levels listed in

§ 141.66, averages of data shall be used and shall be rounded to the same  num- ber of significant figures as  the  max- imum contaminant level for the sub- stance  in  question.

- The State has the authority to de- termine compliance or initiate enforce- ment action based upon analytical re- sults or other information compiled by their sanctioned representatives and agencies.

[41 FR 28404, July 9, 1976, as amended at 45

FR  57345,  Aug.  27,  1980;  62  FR  10173,  Mar.  5,

1997;  65  FR  76745,  Dec.  7,  2000;  67  FR  65250,

Oct. 23, 2002; 69 FR 38855, June 29, 2004; 69 FR

52180, Aug. 25, 2004; 72 FR 11245, Mar. 12, 2007;

74 FR 30958, June 29, 2009]

##### § 141.26 Monitoring frequency and compliance requirements for radio- nuclides in community water sys- tems.

- Monitoring and compliance require- ments for gross alpha particle activity, ra- dium-226, radium-228, and uranium. (1) Community   water   systems   (CWSs) must conduct initial monitoring to de- termine compliance with § 141.66(b), (c), and (e) by December 31, 2007. For the purposes of monitoring for gross alpha particle activity,  radium-226,  radium- 228, uranium, and beta particle and photon radioactivity in drinking water, ‘‘detection     limit’’     is     defined     as     in

§ 141.25(c).

- Applicability and sampling location for existing community water systems or sources. All existing CWSs using ground water, surface water or systems using both ground and surface water (for the purpose of this section hereafter re- ferred to as systems) must sample at every entry point to the distribution system that is representative of all sources being used (hereafter called a sampling point) under normal oper- ating  conditions.  The  system   must take each sample at the same sampling point unless conditions make another sampling point more representative of each source or the State has designated a distribution system location, in ac- cordance with paragraph (a)(2)(ii)(C) of this  section.

- Applicability and sampling location for new community water systems or sources. All new CWSs or CWSs that use a new source of water must begin to conduct initial monitoring for the new source  within  the  first  quarter  after

#### § 141.26

initiating use of the source. CWSs must conduct more frequent monitoring when ordered by the State in the event of possible contamination or when changes in the distribution system or treatment processes occur which may increase the concentration of radioac- tivity in finished water.

- Initial monitoring: Systems must conduct initial monitoring for gross alpha particle activity, radium-226, ra- dium-228, and uranium as follows:

  - Systems without acceptable his- torical data, as defined below, must collect four consecutive quarterly sam- ples at all sampling points before De- cember 31, 2007.

  - Grandfathering of data: States may allow historical monitoring data collected at a sampling point to satisfy the initial monitoring requirements for that sampling point, for the following situations.

- To satisfy initial monitoring re- quirements, a community water  sys- tem having only one entry point to the distribution system may use the moni- toring data from the last compliance monitoring period that began between June 2000 and December 8, 2003.

- To satisfy initial monitoring re- quirements, a community water sys- tem with multiple entry points and having appropriate historical moni- toring data for each entry point to the distribution system may use the moni- toring data from the last compliance monitoring period that began between June 2000 and December 8, 2003.

- To satisfy initial monitoring re- quirements, a community water  sys- tem with  appropriate  historical  data for a representative point in the dis- tribution system may use the moni- toring data from the last compliance monitoring period that began between June 2000 and December 8, 2003, pro- vided that the State finds that the his- torical data satisfactorily demonstrate that each entry point to the distribu- tion system is expected to be in com- pliance based upon the historical data and reasonable assumptions about the variability of contaminant levels be- tween entry points. The State must make a written finding indicating how the data conforms to the these require- ments.

#### 40 CFR Ch. I (7–1–17 Edition)

  - For gross alpha particle activity, uranium, radium-226, and radium-228 monitoring, the State may waive the final two quarters of initial monitoring for a sampling point if the results  of the samples from the previous two quarters are below the detection limit.

  - If the average of the initial moni- toring results for a  sampling point is above the MCL, the system must col- lect and analyze quarterly samples at that sampling point until the system has results from four consecutive quar- ters that are at or below the MCL, un- less the system enters into another schedule as part of a formal compli- ance agreement with the State.

- Reduced monitoring: States may allow community water systems to re- duce the future frequency of moni- toring from once every three years to once every six or nine years at each sampling point, based on the following criteria.

- If the average of the initial moni- toring results for each contaminant (i.e., gross alpha particle activity, ura- nium, radium-226, or radium-228) is below the detection limit specified in Table B, in § 141.25(c)(1), the system must collect and analyze for that con- taminant using at least one sample at that sampling point every nine years.

- For gross alpha particle activity and uranium, if the average of the ini- tial monitoring results for each con- taminant is at or above the detection limit but at or below 1⁄2 the MCL, the system must collect and analyze for that contaminant using at least one sample at that sampling point every six years. For combined radium-226 and radium-228, the analytical results must be combined. If the average of the com- bined initial monitoring results for ra- dium-226 and radium-228 is at or above the detection limit but at or below 1⁄2 the MCL, the system must collect and analyze for that contaminant using at least one sample at that  sampling point every six years.

- For gross alpha particle activity and uranium, if the average of the ini- tial monitoring results for each con- taminant is above 1⁄2 the MCL but at or below the MCL, the system must col- lect and analyze at least one sample at that sampling point every three years. For combined radium-226 and radium-

#### Environmental Protection Agency	§ 141.26

228, the analytical results must be combined. If the average of the com- bined initial monitoring results for ra- dium-226 and radium-228 is above 1⁄2 the MCL but at or below the MCL, the sys- tem must collect and analyze at least one sample at that sampling point every three years.

- Systems must use the samples collected during the reduced moni- toring period to determine the moni- toring frequency for subsequent moni- toring periods (e.g., if a system’s sam- pling point is on a nine year moni- toring period, and the sample result is above 1⁄2 MCL, then the  next  moni- toring period for that sampling point is three years).

- If a system has a monitoring re- sult that exceeds the MCL while on re- duced monitoring, the system must collect and analyze quarterly samples at that sampling point until the sys- tem has results from four consecutive quarters that are below the MCL, un- less the system enters into another schedule as part of a formal compli- ance agreement with the State.

- Compositing: To fulfill quarterly monitoring requirements for gross alpha particle activity, radium-226, ra- dium-228, or uranium, a system may composite up to four consecutive quar- terly samples from a single entry point if analysis is done within a year of the first sample. States will treat analyt- ical results from the composited as the average analytical result to determine compliance with the MCLs and the fu- ture monitoring frequency. If the ana- lytical result from the composited sample is greater  than  1⁄2  MCL,  the State may direct the system to take additional quarterly samples before al- lowing the system to sample under a reduced monitoring schedule.

- A gross alpha particle activity measurement may be substituted for the required radium-226 measurement provided that the measured gross alpha particle activity does not exceed 5 pCi/

l. A gross  alpha particle activity meas- urement may be substituted for the re- quired uranium measurement provided that the measured gross alpha particle activity does not exceed 15 pCi/l. The gross alpha measurement shall have a confidence interval of 95% (1.65s, where s is  the  standard  deviation  of  the  net

counting rate of the sample) for ra- dium-226 and uranium. When a system uses a gross alpha particle activity measurement in lieu of a radium-226 and/or uranium measurement, the gross alpha particle activity analytical result will be used to determine the fu- ture  monitoring  frequency  for  radium-

226 and/or uranium. If the gross alpha particle activity result is less than de- tection, 1⁄2 the detection limit will be used to determine compliance and the future monitoring frequency.

- Monitoring and compliance require- ments for beta particle and photon radio- activity. To determine compliance with the   maximum   contaminant   levels   in

§ 141.66(d) for beta particle and photon radioactivity, a system must  monitor at a frequency as follows:

  - Community water systems (both surface and ground water) designated by the State as vulnerable must sample for beta particle and photon radioac- tivity. Systems must collect quarterly samples for beta emitters and annual samples for tritium and strontium-90 at each entry point to the distribution system (hereafter called a sampling point), beginning within one quarter after being notified by the State. Sys- tems already designated by the State must continue to sample until  the State reviews and either reaffirms or removes the designation.

    - If the gross beta particle activity minus the naturally occurring potas- sium-40 beta particle activity at a sam- pling point has a running annual aver- age (computed quarterly) less than or equal to 50 pCi/L (screening level), the State may reduce the frequency of monitoring at that sampling point to once every 3 years. Systems must col- lect all samples required in paragraph (b)(1) of this section during the reduced monitoring period.

    - For systems in the vicinity of a nuclear facility, the State may allow the CWS to utilize environmental sur- veillance data collected by the nuclear facility in lieu of monitoring at the system’s entry point(s), where the State determines if such data is appli- cable to a particular water system. In the event that there is a release from a nuclear facility, systems which are using surveillance data must begin monitoring  at  the  community  water

#### § 141.26

system’s  entry  point(s)  in  accordance with paragraph (b)(1) of this section.

  - Community water systems (both surface and ground water) designated by the State as utilizing waters con- taminated by effluents from nuclear fa- cilities must sample for beta particle and photon radioactivity. Systems must collect quarterly samples for beta emitters and iodine-131 and annual samples for tritium and strontium-90 at each entry point to the distribution system (hereafter called a sampling point), beginning within one quarter after being notified by the State. Sys- tems already designated by the State as systems using waters contaminated by effluents from nuclear facilities must continue to sample until  the State reviews and either reaffirms or removes the designation.

    - Quarterly monitoring for gross beta particle activity shall be based on the analysis of monthly samples or the analysis of a composite of three month- ly samples. The former is rec- ommended.

    - For iodine-131, a composite of five consecutive daily samples shall be ana- lyzed once each quarter. As ordered by the State, more frequent monitoring shall be conducted when iodine-131 is identified in the finished water.

    - Annual monitoring for stron- tium-90 and tritium shall be conducted by means of the analysis of a com- posite of four consecutive quarterly samples or analysis of four quarterly samples. The latter procedure is rec- ommended.

    - If the gross beta particle activity minus the naturally occurring potas- sium-40 beta particle activity at a sam- pling point has a running annual aver- age (computed quarterly) less than or equal to 15 pCi/L (screening level), the State may reduce the frequency of monitoring at that sampling point to every 3  years.  Systems  must  collect the same type of samples required in paragraph (b)(2) of this section during the reduced monitoring period.

    - For systems in the vicinity of a nuclear facility, the State may allow the CWS to utilize environmental sur- veillance data collected by the nuclear facility in lieu of monitoring at the system’s entry point(s), where the State determines if such data is appli-

#### 40 CFR Ch. I (7–1–17 Edition)

cable to a particular water system. In the event that there is a release from a nuclear facility, systems which are using surveillance data must begin monitoring at the community water system’s entry point(s) in accordance with paragraph (b)(2) of this section.

  - Community water systems des- ignated by the  State  to  monitor  for beta particle and photon radioactivity can not apply to the State for a waiver from the monitoring frequencies speci- fied in paragraph (b)(1) or (b)(2) of this section.

  - Community water systems may analyze for naturally occurring potas- sium-40 beta particle activity from the same or equivalent sample used for the gross beta particle activity analysis. Systems are allowed to subtract the potassium-40 beta particle activity value from the total gross beta particle activity value to determine if the screening level is exceeded. The potas- sium-40 beta particle activity must be calculated by multiplying elemental potassium concentrations (in mg/L) by a factor of 0.82.

  - If the gross beta particle activity minus the naturally occurring potas- sium-40 beta particle activity exceeds the appropriate  screening  level, an analysis of the sample must be per- formed to identify the major radio- active constituents present in the sam- ple and the appropriate doses must be calculated and summed to determine compliance with § 141.66(d)(1), using the formula in § 141.66(d)(2). Doses must also be calculated and combined for measured levels of tritium and stron- tium to determine compliance.

  - Systems must monitor monthly at the sampling point(s) which exceed the   maximum   contaminant   level   in

§ 141.66(d) beginning  the  month  after the exceedance occurs. Systems must continue monthly monitoring until the system has established, by a rolling av- erage of 3  monthly  samples,  that  the MCL is being met. Systems who estab- lish that the MCL is being  met  must return  to  quarterly  monitoring  until they  meet  the  requirements   set   forth in paragraph (b)(1)(i) or (b)(2)(iv) of this section.

- General monitoring and compliance requirements  for  radionuclides.  (1)  The

#### Environmental Protection Agency	§ 141.29

State may require more frequent moni- toring than specified in paragraphs (a) and (b) of this section, or may require confirmation samples at its discretion. The results of the initial and confirma- tion samples will be averaged for use in compliance determinations.

- Each public water systems shall monitor at the time designated by the State during each compliance period.

- Compliance:	Compliance	with

§ 141.66 (b) through (e) will be deter- mined based on the analytical result(s) obtained at each sampling point. If one sampling point is in  violation  of  an MCL, the system is in violation of the MCL.

- For systems monitoring more than once per year, compliance with the MCL is determined by a running annual average at each sampling point. If the average of any sampling point is greater than the MCL, then the system is out of compliance with the MCL.

- For systems monitoring more than once per year, if any sample re- sult will cause the running average to exceed the MCL at any sample point, the system is out of compliance with the MCL immediately.

- Systems must include all sam- ples taken and analyzed under the pro- visions of this section in determining compliance, even if that number is greater than the minimum required.

- If a system does not collect all required samples when compliance is based on a running annual average of quarterly samples, compliance will be based on the running average of the samples  collected.

- If a sample result is less than the detection limit, zero will be used to calculate the annual average, unless a gross alpha particle activity is being used in lieu of radium-226 and/or ura- nium. If  the gross alpha  particle  activ- ity result is less than detection, 1⁄2 the detection limit will be used to  cal- culate the annual average.

- States have the discretion to de- lete results of obvious sampling or ana- lytic errors.

- If the MCL for radioactivity  set forth in § 141.66 (b) through (e) is ex- ceeded, the operator of a community water system must give notice to the State  pursuant  to  § 141.31  and  to  the

public as required by subpart Q of this part.

[65 FR 76745, Dec. 7, 2000, as amended at 69

FR 38855, June 29, 2004]

##### § 141.27   Alternate	analytical	tech- niques.

(a) With the written permission of the State, concurred in by the Admin- istrator of the U.S. EPA, an alternate analytical technique may be employed. An alternate technique shall be accept- ed only if it is substantially equivalent to the prescribed test in both precision and accuracy as it relates to the deter- mination of compliance with any MCL. The use of the alternate analytical technique shall not decrease the fre- quency of monitoring required by this part.

[45 FR 57345, Aug. 27, 1980]

##### § 141.28   Certified laboratories.

- For the purpose of determining compliance with § 141.21 through 141.27, 141.30, 141.40, 141.74, 141.89 and 141.402, samples may be considered only if they have been analyzed by a laboratory certified by the  State except that measurements of alkalinity, calcium, conductivity, disinfectant residual, orthophosphate, pH,  silica,  tempera- ture  and  turbidity  may  be   performed by  any  person  acceptable  to  the  State.

- Nothing in this part shall be con- strued to preclude  the  State  or  any duly designated representative of the State from taking samples or from using the results from such samples to determine compliance by a supplier of water with the applicable requirements of this part.

[45 FR 57345, Aug. 27, 1980; 47 FR 10999, Mar.

12, 1982, as amended at 59 FR 34323, July 1,

1994;  64  FR  67465,  Dec.  1,  1999;  71  FR  65651,

Nov. 8, 2006]

##### § 141.29   Monitoring	of	consecutive public water systems.

When a public water system supplies water to one or more other public water systems, the State may modify the monitoring requirements imposed by this part to the extent that the interconnection of the systems justi- fies treating them as a single  system for monitoring purposes. Any modified

#### Pt. 141, Subpt. C, App. A

monitoring shall be conducted pursu- ant to a schedule specified by the State and concurred in by the Administrator

#### 40 CFR Ch. I (7–1–17 Edition)

of  the  U.S.  Environmental  Protection Agency.

APPENDIX A TO SUBPART C OF PART 141—ALTERNATIVE TESTING METHODS APPROVED FOR ANALYSES UNDER THE SAFE DRINKING WATER ACT

Only the editions stated in the following table are approved.

ALTERNATIVE TESTING METHODS FOR CONTAMINANTS LISTED AT 40 CFR 141.21(f)(3)

| Organism | Methodology | SM 21st Edition 1 | SM 22nd Edi- tion 28 | SM Online 3 | Other |
| --- | --- | --- | --- | --- | --- |
| Total Coliforms ...... | Total Coliform Fermentation Technique. Total Coliform Membrane Filter Technique. Presence-Ab- sence (P–A) Coliform Test. ONPG–MUG Test Colitag TM ............. Tecta EC/TC 33 .... | 9221 A, B ............ 9222 A, B, C. 9221 D. 9223 ..................... .............................. .............................. | 9221 A, B ............ 9223 B ................. .............................. .............................. | 9221 A,B–06. 9223 B–04. .............................. .............................. | Modified Colitag TM 13 |

ALTERNATIVE TESTING METHODS FOR CONTAMINANTS LISTED AT 40 CFR 141.21(f)(5)

| Organism | Methodology | SM 22nd Edition 28 | SM Online 3 |
| --- | --- | --- | --- |
| Fecal Coliforms ............................... | Fecal Coliform Procedure .............. | 9221 E ............................................ | 9221 E–06 |

Pt. 141, Subpt. C, App. A

435

Environmental Protection Agency

ALTERNATIVE TESTING METHODS FOR CONTAMINANTS LISTED AT 40 CFR 141.21(f)(6)

| Organism | Methodology | SM 20th Edition 6 | SM 21st Edition 1 | SM 22nd Edition 28 | SM Online 3 | Other |
| --- | --- | --- | --- | --- | --- | --- |
| E.coli .................................................. | ONPG–MUG Test ............................. | 9223 B | 9223 B | 9223 B | 9223 B–97, B–04 | Modified Colitag TM 13 |
|  | Colitag TM ........................................... | ........................ | ........................ | ........................ | .................................... |  |
|  | Tecta EC/TC 33 .................................. | ........................ | ........................ | ........................ | .................................... |  |

#### Pt. 141, Subpt. C, App. A

40 CFR Ch. I (7–1–17 Edition)

ALTERNATIVE TESTING METHODS FOR CONTAMINANTS LISTED AT 40 CFR 141.23(k)(1)

| Contami- nant | Methodology | EPA method | SM 21st edition 1 | SM 22nd edition 28 | SM online 3 | ASTM 4 | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Alkalinity ... Antimony .. Arsenic ..... Barium ..... Beryllium .. Cadmium Calcium .... Chromium Copper ..... | Titrimetric ....................... Hydride—Atomic Ab- sorption. Atomic Absorption; Fur- nace. Axially viewed induc- tively coupled plasma- atomic emission spec- trometry (AVICP– AES). Atomic Absorption; Fur- nace. Hydride Atomic Absorp- tion. Axially viewed induc- tively coupled plasma- atomic emission spec- trometry (AVICP– AES). Inductively Coupled Plasma. Atomic Absorption; Di- rect. Atomic Absorption; Fur- nace. Axially viewed induc- tively coupled plasma- atomic emission spec- trometry (AVICP– AES). Inductively Coupled Plasma. Atomic Absorption; Fur- nace. Axially viewed induc- tively coupled plasma- atomic emission spec- trometry (AVICP– AES). Atomic Absorption; Fur- nace. Axially viewed induc- tively coupled plasma- atomic emission spec- trometry (AVICP– AES). EDTA Titrimetric ............ Atomic Absorption; Di- rect Aspiration. Inductively Coupled Plasma. Axially viewed induc- tively coupled plas- ma–atomic emission spectrometry (AVICP– AES). Ion Chromatography ..... Inductively Coupled Plasma. Atomic Absorption; Fur- nace. Axially viewed induc- tively coupled plasma- atomic emission spec- trometry (AVICP– AES). Atomic Absorption; Fur- nace. | ........................... ........................... ........................... 200.5, Revision 4.2.2. ........................... ........................... 200.5, Revision 4.2 2. ........................... ........................... ........................... 200.5, Revision 4.2 2. ........................... ........................... 200.5, Revision 4.2 2. ........................... 200.5, Revision 4.2 2. ........................... ........................... ........................... 200.5, Revision 4.2.2. ........................... ........................... ........................... 200.5, Revision 4.2 2. ........................... | 2320 B ..... .................. 3113 B ..... .................. 3113 B ..... 3114 B ..... 3120 B ..... 3111 D ..... 3113 B ..... 3120 B ..... 3113 B ..... 3113 B ..... 3500–Ca B 3111 B ..... 3120 B ..... .................. .................. 3120 B ..... 3113 B ..... 3113 B ..... | 2320 B ..... .................. 3113 B ..... .................. 3113 B ..... 3114 B ..... 3120 B. 3111 D. 3113 B ..... 3120 B. 3113 B ..... 3113 B ..... 3500–Ca B 3111 B ..... 3120 B ..... .................. .................. 3120 B. 3113 B ..... 3113 B ..... | .................. .................. 3113 B– 04, B–10. . 3113 B– 04, B–10. 3114 B–09 3113 B– 04, B–10. 3113 B– 04, B–10. 3113 B– 04, B–10. .................. .................. . . .................. 3113 B– 04, B–10. 3113 B– 04, B–10. | D1067–06 B, 11 B D 3697– 07, –12. D 2972–08 C. D 2972–08 B. D 3645–08 B. D 511–09, –14 A. D 511–90, –14 B. D 6919–09. D 1688– 07, –12 C. |  |

#### Environmental Protection Agency	Pt. 141, Subpt. C, App. A

ALTERNATIVE TESTING METHODS FOR CONTAMINANTS LISTED AT 40 CFR 141.23(k)(1)—Continued

| Contami- nant | Methodology | EPA method | SM 21st edition 1 | SM 22nd edition 28 | SM online 3 | ASTM 4 | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Conduc- tivity. Cyanide ... Fluoride .... Lead ......... Magne- sium. Mercury .... Nickel ....... Nitrate ...... | Atomic Absorption; Di- rect Aspiration. Inductively Coupled Plasma. Axially viewed induc- tively coupled plas- ma–atomic emission spectrometry (AVICP– AES). Colorimetric ................... Conductance ................. Manual Distillation fol- lowed by. Spectrophotometric, Amenable. Spectrophotometric Manual. Selective Electrode ....... Headspace Gas Chro- matography/Mass Spectrometry. Ion Chromatography ..... Manual Distillation; Col- orimetric SPADNS. Manual Electrode .......... Automated Alizarin ........ Arsenite-Free Colori- metric SPADNS. Atomic Absorption; Fur- nace. Axially viewed induc- tively coupled plasma- atomic emission spec- trometry (AVICP– AES). Atomic Absorption ......... Inductively Coupled Plasma. Complexation Titrimetric Methods. Axially viewed induc- tively coupled plasma- atomic emission spec- trometry (AVICP– AES). Ion Chromatography ..... Manual, Cold Vapor ...... Inductively Coupled Plasma. Atomic Absorption; Di- rect. Atomic Absorption; Fur- nace. Axially viewed induc- tively coupled plasma- atomic emission spec- trometry (AVICP– AES). Ion Chromatography ..... | ........................... ........................... 200.5, Revision 4.2.2. ........................... ........................... ........................... ........................... ........................... ........................... ........................... ........................... ........................... ........................... ........................... ........................... ........................... 200.5, Revision 4.2 2. ........................... ........................... ........................... 200.5, Revision 4.2.2. ........................... ........................... ........................... ........................... ........................... 200.5, Revision 4.2 2. ........................... | 3111 B ..... 3120 B ..... .................. .................. 2510 B ..... .................. 4500–CN¥ G. 4500–CN¥ E. 4500–CN¥ F. .................. 4110 B ..... 4500–F¥ B, D. 4500–F¥ C. 4500–F¥ E. .................. 3113 B ..... 3111 B ..... 3120 B ..... 3500–Mg B. .................. .................. 3112 B ..... 3120 B ..... 3111 B ..... 3113 B ..... 4110 B ..... | 3111 B ..... 3120 B ..... .................. .................. 2510 B ..... .................. 4500–CN¥ G. 4500–CN¥ E. 4500–CN¥ F. .................. 4110 B ..... 4500–F¥ B, D. 4500–F¥ C. 4500–F¥ E. .................. 3113 B ..... 3111 B ..... 3120 B ..... 3500–Mg B. .................. .................. 3112 B ..... 3120 B. 3111 B. 3113 B ..... 4110 B ..... | .................. . . .................. .................. .................. .................. .................. .................. .................. .................. .................. 3113 B– 04, B–10. .................. . .................. . .................. 3112 B–09 3113 B– 04, B–10. .................. | D 1688– 07, –12 A. .................. D 1125–14 A. D 2036–06 A D 2036–06 B D2036–06 A .................. D 4327–11. D 1179– 04, 10 B. .................. D 3559–08 D. D 511–09, ¥14 B. D 511–09, –14 A. D 6919–09. D 3223–12. D 4327–11. | Hach Method 8026 35 Hach Meth- od 10272.36 ME355.01 7 Hach SPADNS 2 Method 10225 22 |

#### Pt. 141, Subpt. C, App. A

40 CFR Ch. I (7–1–17 Edition)

ALTERNATIVE TESTING METHODS FOR CONTAMINANTS LISTED AT 40 CFR 141.23(k)(1)—Continued

| Contami- nant | Methodology | EPA method | SM 21st edition 1 | SM 22nd edition 28 | SM online 3 | ASTM 4 | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Nitrite ....... Orthophos- phate. pH ............ Selenium .. Silica ........ Sodium .... | Automated Cadmium Reduction. Manual Cadmium Re- duction. Ion Selective Electrode Reduction/Colorimetric .. Colorimetric; Direct ........ Ion Chromatography ..... Automated Cadmium Reduction. Manual Cadmium Re- duction. Spectrophotometric ....... Reduction/Colorimetric .. Ion Chromatography ..... Colorimetric, ascorbic acid, single reagent. Colorimetric, Automated, Ascorbic Acid. Electrometric ................. Hydride-Atomic Absorp- tion. Atomic Absorption; Fur- nace. Axially viewed induc- tively coupled plasma- atomic emission spec- trometry (AVICP– AES). Colorimetric ................... Molybdosilicate .............. Heteropoly blue ............. Automated for Molyb- date-reactive Silica. Axially viewed induc- tively coupled plasma- atomic emission spec- trometry (AVICP– AES). Inductively Coupled Plasma. Atomic Absorption; Di- rect Aspiration. | ........................... ........................... ........................... ........................... ........................... ........................... ........................... ........................... ........................... ........................... ........................... ........................... ........................... ........................... ........................... ........................... 200.5, Revision 4.2 2. ........................... ........................... ........................... ........................... 200.5, Revision 4.2 2 ........................... ........................... | 4500– NO3 F. 4500– NO3 E. 4500– NO3 D. .................. .................. 4110 B ..... 4500– NO3 F. 4500– NO3 E. 4500– NO2 B. .................. 4110 B ..... 4500–P E 4500–P F 4500– H + B. 3114 B ..... 3113 B ..... .................. 4500-SiO2 C. 4500–SiO2 D. 4500–SiO2 E. 3120 B ..... 3111 B ..... | 4500– NO3 F. 4500– NO3 E. 4500– NO3 D. .................. .................. 4110 B ..... 4500– NO3 F. 4500– NO3 E. 4500– NO2 B. .................. 4110 B ..... 4500–P E 4500–P F 4500– H + B. 3114 B ..... 3113 B ..... .................. 4500-SiO2 C. 4500–SiO2 D. 4500–SiO2 E. 3120 B 3111 B | . . . .................. .................. .................. . . . .................. .................. 4500–P E– 99. 4500–P F– 99. .................. 3114 B–09 3113 B– 04, B–10. .................. | .................. .................. D 4327–11. .................. D 4327–11. .................. D 1293–12 D 3859–08 A. D 3859–08 B. D859–05, 10 | Systea Easy (1-Rea- gent) 8 NECi Ni- trate-Re- ductase.40 Hach TNTplus TM 835/836 Method 10206.23 Systea Easy (1-Rea- gent) 8 NECi Ni- trate-Re- ductase.40 Thermo-Fish- er Discrete Analyzer.41 |

#### Environmental Protection Agency	Pt. 141, Subpt. C, App. A

ALTERNATIVE TESTING METHODS FOR CONTAMINANTS LISTED AT 40 CFR 141.23(k)(1)—Continued

| Contami- nant | Methodology | EPA method | SM 21st edition 1 | SM 22nd edition 28 | SM online 3 | ASTM 4 | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Tempera- ture. | Axially viewed induc- tively coupled plasma- atomic emission spec- trometry (AVICP– AES). Ion Chromatography ..... Thermometric ................ | 200.5, Revision 4.2 2 ........................... ........................... | .................. 2550 ......... | .................. 2550 ......... | .................. 2550–10. | D 6919–09 |  |

40 CFR Ch. I (7–1–17 Edition)

440

Pt. 141, Subpt. C, App. A

ALTERNATIVE TESTING METHODS FOR CONTAMINANTS LISTED AT 40 CFR 141.24(e)(1)

| Contaminant | Methodology | EPA method | SM 21st edition 1 | SM 22nd edition 28 | SM online 3 |
| --- | --- | --- | --- | --- | --- |
| Benzene ................................................... Carbon tetrachloride ................................. Chlorobenzene ......................................... 1,2-Dichlorobenzene ................................ 1,4-Dichlorobenzene ................................ 1,2-Dichloroethane ................................... cis-Dichloroethylene ................................. trans-Dichloroethylene ............................. Dichloromethane ...................................... 1,2-Dichloropropane ................................. Ethylbenzene ............................................ Styrene ..................................................... Tetrachloroethylene .................................. 1,1,1-Trichloroethane ............................... Trichloroethylene ...................................... Toluene .................................................... 1,2,4-Trichlorobenzene ............................ 1,1-Dichloroethylene ................................ 1,1,2-Trichlorethane ................................. Vinyl chloride ............................................ Xylenes (total) .......................................... 2,4-D ......................................................... 2,4,5-TP (Silvex) ...................................... Alachlor .................................................... Atrazine .................................................... Benzo(a)pyrene ........................................ Carbofuran ............................................... Chlordane ................................................. Dalapon .................................................... Di(2-ethylhexyl)adipate ............................. Di(2-ethylhexyl)phthalate .......................... | Purge & trap/Gas Chromatography/Mass Spectrometry ......... Purge & trap/Gas Chromatography/Mass Spectrometry ......... Purge & trap/Gas Chromatography/Mass Spectrometry ......... Purge & trap/Gas Chromatography/Mass Spectrometry ......... Purge & trap/Gas Chromatography/Mass Spectrometry ......... Purge & trap/Gas Chromatography/Mass Spectrometry ......... Purge & trap/Gas Chromatography/Mass Spectrometry ......... Purge & trap/Gas Chromatography/Mass Spectrometry ......... Purge & trap/Gas Chromatography/Mass Spectrometry ......... Purge & trap/Gas Chromatography/Mass Spectrometry ......... Purge & trap/Gas Chromatography/Mass Spectrometry ......... Purge & trap/Gas Chromatography/Mass Spectrometry ......... Purge & trap/Gas Chromatography/Mass Spectrometry ......... Purge & trap/Gas Chromatography/Mass Spectrometry ......... Purge & trap/Gas Chromatography/Mass Spectrometry ......... Purge & trap/Gas Chromatography/Mass Spectrometry ......... Purge & trap/Gas Chromatography/Mass Spectrometry ......... Purge & trap/Gas Chromatography/Mass Spectrometry ......... Purge & trap/Gas Chromatography/Mass Spectrometry ......... Purge & trap/Gas Chromatography/Mass Spectrometry ......... Purge & trap/Gas Chromatography/Mass Spectrometry ......... Gas Chromatography/Electron Capture Detection (GC/ECD) Gas Chromatography/Electron Capture Detection (GC/ECD) Solid Phase Extraction/Gas Chromatography/Mass Spec- trometry (GC/MS). Liquid Chromatography Electrospray Ionization Tandem Mass Spectrometry (LC/ESI–MS/MS). Solid Phase Extraction/Gas Chromatography/Mass Spec- trometry (GC/MS). Solid Phase Extraction/Gas Chromatography/Mass Spec- trometry (GC/MS). High-performance liquid chromatography (HPLC) with post- column derivatization and fluorescence detection. Solid Phase Extraction/Gas Chromatography/Mass Spec- trometry (GC/MS). Ion Chromatography Electrospray Ionization Tandem Mass Spectrometry (IC–ESI–MS/MS). Gas Chromatography/Electron Capture Detection (GC/ECD) Solid Phase Extraction/Gas Chromatography/Mass Spec- trometry (GC/MS). Solid Phase Extraction/Gas Chromatography/Mass Spec- trometry (GC/MS). | 524.3,9 524.4 29 524.3,9 524.4 29 524.3,9 524.4 29 524.3,9 524.4 29 524.3,9 524.4 29 524.3,9 524.4 29 524.3,9 524.4 29 524.3,9 524.4 29 524.3,9 524.4 29 524.3,9 524.4 29 524.3,9 524.4 29 524.3,9 524.4 29 524.3,9 524.4 29 524.3,9 524.4 29 524.3,9 524.4 29 524.3,9 524.4 29 524.3,9 524.4 29 524.3,9 524.4 29 524.3,9 524.4 29 524.3,9 524.4 29 524.3,9 524.4 29 ........................................ ........................................ 525.3 24 536 25 525.3, 24 523 26 525.3 24 525.3 24 557 14 ........................................ 525.3 24 525.3 24 | 6640 B ............. 6640 B ............. 6610 B ............. 6640 B ............. | 6640 B ............. 6640 B ............. 6610 B ............. 6640 B ............. | 6640 B–01, B– 06. 6640 B–01, B– 06. 6610 B–04. 6640 B–01, B– 06. |

Environmental Protection Agency

Pt. 141, Subpt. C, App. A

441

Dibromochloropropane (DBCP) ...............  Purge & trap/Gas Chromatography/Mass Spectrometry .........	524.3 9

Dinoseb ....................................................   Gas Chromatography/Electron Capture Detection (GC/ECD)	........................................   6640 B  .............   6640 B  .............   6640 B–01, B–

06.

Endrin .......................................................

Heptachlor Epoxide ..................................

Pentachlorophenol  ...................................

Solid  Phase  Extraction/Gas  Chromatography/Mass  Spec-

trometry (GC/MS).

Purge & trap/Gas Chromatography/Mass Spectrometry ......... High-Performance Liquid Chromatography (HPLC) with Post-

Column Derivatization and Fluorescence Detection.

Solid  Phase  Extraction/Gas  Chromatography/Mass  Spec- trometry (GC/MS).

Solid  Phase  Extraction/Gas  Chromatography/Mass  Spec- trometry (GC/MS).

Solid  Phase  Extraction/Gas  Chromatography/Mass  Spec- trometry (GC/MS).

Solid  Phase  Extraction/Gas  Chromatography/Mass  Spec- trometry (GC/MS).

Solid  Phase  Extraction/Gas  Chromatography/Mass  Spec- trometry (GC/MS).

Solid  Phase  Extraction/Gas  Chromatography/Mass  Spec- trometry (GC/MS).

High-performance liquid chromatography (HPLC) with post- column derivatization and fluorescence detection.

Solid  Phase  Extraction/Gas  Chromatography/Mass  Spec- trometry (GC/MS).

Gas Chromatography/Electron Capture Detection (GC/ECD)

525.3 24

Ethyl dibromide (EDB)  .............................

Glyphosate ...............................................

524.3 9

........................................

6651 B  .............   6651 B  .............   6651 B–00, B–

05.

Heptachlor ................................................

525.3 24

525.3 24

Hexachlorobenzene  .................................

525.3 24

Hexachlorocyclo-pentadiene ....................

525.3 24

Lindane .....................................................

525.3 24

Methoxychlor ............................................

525.3 24

Oxamyl .....................................................

6610 B  .............

6610 B  .............

6610 B–04.

PCBs (as Aroclors)  ..................................

525.3 24

........................................

6640 B  .............

6640 B  .............

6640 B–01, B–

06.

Solid  Phase  Extraction/Gas  Chromatography/Mass  Spec-

trometry (GC/MS).

Gas Chromatography/Electron Capture Detection (GC/ECD)

525.3 24

Picloram  ...................................................	........................................

6640 B  .............   6640 B  .............   6640 B–01, B–

06.

Simazine ...................................................

Toxaphene  ...............................................

Liquid   Chromatography   Electrospray   Ionization   Tandem

Mass Spectrometry (LC/ESI–MS/MS).

Solid  Phase  Extraction/Gas  Chromatography/Mass  Spec- trometry (GC/MS).

Solid  Phase  Extraction/Gas  Chromatography/Mass  Spec- trometry (GC/MS).

Purge & trap/Gas Chromatography/Mass Spectrometry .........

536 25

525.3,24 523 26

525.3 24

Total Trihalomethanes  .............................

524.3,9 524.4 29

Pt. 141, Subpt. C, App. A

40 CFR Ch. I (7–1–17 Edition)

ALTERNATIVE TESTING METHODS FOR CONTAMINANTS LISTED AT 40 CFR 141.25(a)

| Contaminant | Methodology | SM 21st Edi- tion 1 | SM 22nd Edition 28 | ASTM 4 |
| --- | --- | --- | --- | --- |
| Naturally Occurring: | Evaporation ............................................ | 7110 B ............. | 7110 B. | D3454–05 |
| Gross alpha and beta ........... |  |  |  |  |
| Gross alpha .......................... | Coprecipitation ....................................... | 7110 C ............. | 7110 C. |  |
| Radium 226 .......................... | Radon emanation ................................... | 7500–Ra C ...... | 7500–Ra C ...... |  |
|  | Radiochemical ........................................ | 7500–Ra B ...... | 7500–Ra B ...... | D2460–07 |
| Radium 228 .......................... | Radiochemical ........................................ | 7500–Ra D ...... | 7500–Ra D. |  |
| Uranium ................................ | Radiochemical ........................................ | 7500–U B ........ | 7500–U B. |  |
|  | ICP–MS .................................................. | 3125 ................ | .......................... | D5673–05, 10 |
|  | Alpha spectrometry ................................ | 7500–U C ........ | 7500–U C ........ | D3972–09 |
|  | Laser Phosphorimetry ............................ | .......................... | .......................... | D5174–07 |
|  | Alpha Liquid Scintillation Spectrometry | .......................... | .......................... | D6239–09 |
| Man-Made: |  |  |  |  |
| Radioactive Cesium .............. | Radiochemical ........................................ | 7500–Cs B ...... | 7500–Cs B. |  |
|  | Gamma Ray Spectrometry .................... | 7120 ................ | 7120 ................ | D3649–06 |
| Radioactive Iodine ................ | Radiochemical ........................................ | 7500–I B .......... | 7500–I B .......... | D3649–06 |
|  |  | 7500–I C .......... | 7500–I C. |  |
|  |  | 7500–I D .......... | 7500–I D. |  |
|  | Gamma Ray Spectrometry .................... | 7120 ................ | 7120 ................ | D4785–08 |
| Radioactive Strontium 89, 90 | Radiochemical ........................................ | 7500–Sr B ....... | 7500–Sr B. |  |
| Tritium ................................... | Liquid Scintillation .................................. | 7500–3H B ....... | 7500–3H B ....... | D4107–08 |
| Gamma Emitters ................... | Gamma Ray Spectrometry .................... | 7120 ................ | 7120 ................ | D3649–06 |
|  |  | 7500–Cs B ...... | 7500–Cs B ...... | D4785–08 |
|  |  | 7500–I B .......... | 7500–I B .......... |  |

Pt. 141, Subpt. C, App. A

443

Environmental Protection Agency

ALTERNATIVE TESTING METHODS FOR CONTAMINANTS LISTED AT 40 CFR 141.74(a)(1)

| Organism | Methodology | SM 21st Edition 1 | SM 22nd Edition 28 | SM Online 3 | Other |
| --- | --- | --- | --- | --- | --- |
| Total Coliform .......................... Fecal Coliforms ....................... Heterotrophic bacteria ............. Turbidity ................................... | Total Coliform Fermentation Technique. Total Coliform Membrane Fil- ter Technique. ONPG–MUG Test .................. Fecal Coliform Procedure ...... Fecal Coliform Filter Proce- dure. Pour Plate Method ................. Nephelometric Method ........... Laser Nephelometry (on-line) LED Nephelometry (on-line) .. LED Nephelometry (on-line) .. LED Nephelometry (portable) 360Nephelometry ................ | 9221 A, B, C .......................... 9222 A, B, C. 9223 ....................................... 9221 E .................................... 9222 D ................................... 9215 B .................................... 2130 B .................................... ................................................ ................................................ ................................................ ................................................ ................................................ | 9221 A, B, C .......................... 9223 B .................................... 9221 E .................................... 9222 D ................................... 9215 B .................................... 2130 B .................................... ................................................ ................................................ ................................................ ................................................ ................................................ | 9221 A,B,C–06. 9223 B–04. 9221 E–06. 9222 D–06. 9215 B–04. ................................................ ................................................ ................................................ ................................................ ................................................ | Mitchell M5271,10 Mitch- ell M5331, Rev. 1.2.42 Mitchell M5331,11 Mitch- ell M5331, Rev. 1.2.42 AMI Turbiwell.15 Orion AQ4500.12 Hach Method 10258.39 |

#### Pt. 141, Subpt. C, App. A

40 CFR Ch. I (7–1–17 Edition)

ALTERNATIVE TESTING METHODS FOR DISINFECTANT RESIDUALS LISTED AT 40 CFR 141.74(a)(2)

| Residual | Methodology | SM 21st Edition 1 | SM 22nd Edi- tion 28 | ASTM 4 | Other |
| --- | --- | --- | --- | --- | --- |
| Free Chlo- rine. Total Chlo- rine. Chlorine Dioxide. Ozone ....... | Amperometric Titration ......... DPD Ferrous Titrimetric ....... DPD Colorimetric ................. Syringaldazine (FACTS) ...... On-line Chlorine Analyzer .... Amperometric Sensor .......... Indophenol Colorimetric ....... Amperometric Titration ......... Amperometric Titration (Low level measurement). DPD Ferrous Titrimetric ....... DPD Colorimetric ................. Iodometric Electrode ............ On-line Chlorine Analyzer .... Amperometric Sensor .......... Amperometric Titration ......... Amperometric Titration ......... Amperometric Sensor .......... Indigo Method ...................... | 4500–Cl D .......... 4500–Cl F ........... 4500–Cl G .......... 4500–Cl H .......... ............................. ............................. ............................. 4500–Cl D .......... 4500–Cl E .......... 4500–Cl F ........... 4500–Cl G .......... 4500–Cl I ............ ............................. ............................. 4500–ClO2 C ...... 4500–ClO2 E ...... ............................. 4500–O3 B .......... | 4500–Cl D .......... 4500–Cl F. 4500–Cl G .......... 4500–Cl H. ............................. ............................. ............................. 4500–Cl D .......... 4500–Cl E. 4500–Cl F. 4500–Cl G .......... 4500–Cl I. ............................. ............................. 4500–ClO2 C. 4500–ClO2 E. ............................. 4500–O3 B. | D 1253–08, ¥14. ............................. ............................. ............................. ............................. D 1253–08, ¥14. ............................. ............................. ............................. ............................. | Hach Method 10260.31 EPA 334.0.16 ChloroSense.17 Hach Method 10241.34 Hach Method 10260.31 EPA 334.0.16 ChloroSense.17 ChlordioX Plus.32 |

445

Environmental Protection Agency

ALTERNATIVE TESTING METHODS FOR CONTAMINANTS LISTED AT 40 CFR 141.131(b)(1)

| Contaminant | Methodology | EPA Method | ASTM 4 | SM Online 3 | SM 21st Edition 1 | SM 22nd Edition 28 | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| TTHM ............................ HAA5 ............................. Bromate ........................ Chlorite .......................... Chlorite—daily moni- toring as prescribed in 40 CFR 141.132(b)(2)(i)(A). | P&T/GC/MS ............... LLE (diazomethane)/ GC/ECD. Ion Chromatography Electrospray Ioniza- tion Tandem Mass Spectrometry (IC– ESI–MS/MS). Two-Dimensional Ion Chromatography (IC). Ion Chromatography Electrospray Ioniza- tion Tandem Mass Spectrometry (IC– ESI–MS/MS). Chemically Sup- pressed Ion Chro- matography. Electrolytically Sup- pressed Ion Chro- matography. Chemically Sup- pressed Ion Chro- matography. Electrolytically Sup- pressed Ion Chro- matography. Amperometric Titra- tion. Amperometric Sensor | 524.3 9, 524.4 29. .................................... 557 14. 302.0 18. 557 14. .................................... .................................... .................................... .................................... .................................... .................................... | ............................. D 6581–08 A. D 6581–08 B. D 6581–08 A. D 6581–08 B. ............................. ............................. | 6251 B–07 .......... ............................. ............................. | 6251 B ....................... 4500–ClO2 E ............. .................................... | 6251 B. 4500–ClO2 E. .................................... | ChlordioX Plus.32 |

Pt. 141, Subpt. C, App. A

ALTERNATIVE TESTING METHODS FOR DISINFECTANT RESIDUALS LISTED AT 40 CFR 141.131(c)(1)

| Residual | Methodology | SM 21st Edition 1 | SM 22nd Edition 28 | ASTM 4 | Other |
| --- | --- | --- | --- | --- | --- |
| Free Chlorine .......................... | Amperometric Titration ........... | 4500–Cl D .............................. | 4500–Cl D .............................. | D 1253–08, ¥14. | Hach Method 10260.31 |
|  | DPD Ferrous Titrimetric ......... | 4500–Cl F .............................. | 4500–Cl F. |  |  |
|  | DPD Colorimetric ................... | 4500–Cl G .............................. | 4500–Cl G .............................. | ................................................ |  |
|  | Syringaldazine (FACTS) ........ | 4500–Cl H .............................. | 4500–Cl H. |  |  |
|  | Amperometric Sensor ............ | ................................................ | ................................................ | ................................................ | ChloroSense.17 |
|  | On-line Chlorine Analyzer ...... | ................................................ | ................................................ | ................................................ | EPA 334.0.16 |

40 CFR Ch. I (7–1–17 Edition)

446

Pt. 141, Subpt. C, App. A

ALTERNATIVE TESTING METHODS FOR DISINFECTANT RESIDUALS LISTED AT 40 CFR 141.131(c)(1)—Continued

| Residual | Methodology | SM 21st Edition 1 | SM 22nd Edition 28 | ASTM 4 | Other |
| --- | --- | --- | --- | --- | --- |
| Combined Chlorine ................. Total Chlorine .......................... Chlorine Dioxide ...................... | Indophenol Colorimetric ......... Amperometric Titration ........... DPD Ferrous Titrimetric ......... DPD Colorimetric ................... Amperometric Titration ........... Low level Amperometric Titra- tion. DPD Ferrous Titrimetric ......... DPD Colorimetric ................... Iodometric Electrode .............. Amperometric Sensor ............ On-line Chlorine Analyzer ...... Amperometric Method II ........ Amperometric Sensor ............ | ................................................ 4500–Cl D .............................. 4500–Cl F .............................. 4500–Cl G .............................. 4500–Cl D .............................. 4500–Cl E .............................. 4500–Cl F .............................. 4500–Cl G .............................. 4500–Cl I ................................ ................................................ ................................................ 4500–ClO2 E .......................... ................................................ | ................................................ 4500–Cl D .............................. 4500–Cl F. 4500–Cl G .............................. 4500–Cl D .............................. 4500–Cl E. 4500–Cl F. 4500–Cl G .............................. 4500–Cl I. ................................................ ................................................ 4500–ClO2 E. ................................................ | ................................................ D 1253–08, ¥14. ................................................ D 1253–08, ¥14. ................................................ ................................................ ................................................ ................................................ | Hach Method 10241.34 Hach Method 10260.31 Hach Method 10260.31 ChloroSense.17 EPA 334.0.16 ChlordioX Plus 32. |

#### Environmental Protection Agency	Pt. 141, Subpt. C, App. A

ALTERNATIVE TESTING METHODS FOR DISINFECTANT RESIDUALS LISTED AT 40 CFR 141.131(c)(2), IF APPROVED BY THE STATE

| Residual | Methodology | Method |
| --- | --- | --- |
| Free Chlorine ................. | Test Strips .................................................................................................... | Method D99–003 5 |

40 CFR Ch. I (7–1–17 Edition)

448

Pt. 141, Subpt. C, App. A

ALTERNATIVE TESTING METHODS FOR PARAMETERS LISTED AT 40 CFR 141.131(d)

| Parameter | Methodology | SM 21st Edition 1 | SM 22nd Edition 28 | SM Online 3 | EPA | Other |
| --- | --- | --- | --- | --- | --- | --- |
| Total Organic Carbon (TOC) ..... Specific Ultraviolet Absorbance (SUVA). Dissolved Organic Carbon (DOC). Ultraviolet absorption at 254 nm (UV254). | High Temperature Combustion Persulfate-Ultraviolet or Heated Persulfate Oxidation. Wet Oxidation ............................ Ozone Oxidation ........................ Calculation using DOC and UV254 data. High Temperature Combustion Persulfate-Ultraviolet or Heated Persulfate Oxidation. Wet Oxidation ............................ Spectrophotometry ..................... | 5310 B ........ 5310 C ....... 5310 D ....... .................... .................... 5310 B ........ 5310 C ....... 5310 D ....... 5910 B ........ | 5310 B ....... 5310 C ....... 5310 D ....... .................... .................... 5310 B ........ 5310 C ....... 5310 D ....... 5910 B ........ | .................... .................... .................... .................... .................... .................... .................... .................... 5910 B–11 .. | 415.3, Rev 1.2.19. 415.3, Rev 1.2 19 415.3, Rev 1.2.19. .............................. 415.3, Rev 1.2.19. 415.3, Rev 1.2.19. 415.3, Rev 1.2.19. 415.3, Rev 1.2.19. 415.3, Rev 1.2.19 | Hach Method 10267.38 Hach Method 10261.37 |

#### Environmental Protection Agency	Pt. 141, Subpt. C, App. A

ALTERNATIVE TESTING METHODS WITH MRL >0.0010 MG/L FOR MONITORING LISTED AT 40 CFR 141.132(b)(3)(ii)(B)

| Contaminant | Methodology | EPA method |
| --- | --- | --- |
| Bromate ...................... | Two-Dimensional Ion Chromatography (IC) ......................................................... Ion Chromatography Electrospray Ionization Tandem Mass Spectrometry (IC– ESI–MS/MS). | 302.0 18 557 14 |

ALTERNATIVE TESTING METHODS FOR CONTAMINANTS LISTED AT 40 CFR 141.402(c)(2)

| Organism | Methodology | SM 20th Edition 6 | SM 21st Edition 1 | SM 22nd Edition 28 | SM Online 3 | Other |
| --- | --- | --- | --- | --- | --- | --- |
| E. coli ............ Enterococci ... Coliphage ...... | Colilert ........ Colisure ...... Colilert-18 ..... Readycult ... Colitag .......... Chromocult EC–MUG ...... Tecta EC/ TC 33. Multiple-Tube Technique. Two-Step En- richment Presence- Absence Procedure. | ........................... ........................... 9223 B ............... ........................... ........................... ........................... ........................... ........................... ........................... | 9223 B ............... 9223 B ............... 9223 B ............... ........................... ........................... ........................... ........................... ........................... ........................... | 9223 B ............... 9223 B ............... 9223 B ............... ........................... ........................... ........................... 9221 F ............... ........................... ........................... | 9223 B–97, B– 04. 9223 B–97, B– 04. 9223 B–97, B– 04. ........................... ........................... ........................... 9221 F–06. 9230 B–04. ........................... | Readycult 20. Modified Colitag TM 13. Chromocult 21. Fast Phage 30 |

ALTERNATIVE TESTING METHODS FOR CONTAMINANTS LISTED AT 40 CFR 141.704(a)

| Organism | Methodology | EPA Method |
| --- | --- | --- |
| Cryptosporidium .............. | Filtration/Immunomagnetic Separation/Immunofluorescence Assay Micros- copy. | 1623.1 27 |

ALTERNATIVE TESTING METHODS FOR CONTAMINANTS LISTED AT 40 CFR 141.704(b)

| Organism | Methodology | SM 20th edition 6 |
| --- | --- | --- |
| E. coli ..................... | Membrane Filtration, Two Step ............................................................................ | 9222 D/9222 G |

ALTERNATIVE TESTING METHODS FOR CONTAMINANTS LISTED AT 40 CFR 141.852(a)(5)

| Organism | Methodology cat- egory | Method | SM 20th, 21st edi- tions 16 | SM 22nd Edition 28 | SM Online 3 |
| --- | --- | --- | --- | --- | --- |
| Total Coliforms ........ Escherichia coli ........ | Lactose Fermenta- tion Methods. Enzyme Substrate Methods. Escherichia coli Pro- cedure (following Lactose Fer- mentation Meth- ods). Enzyme Substrate Methods. | Standard Total Coli- form Fermentation Technique. Colilert .................. Colisure ................ Colilert-18 ............. Tecta EC/TC .33 EC–MUG medium .. Colilert .................. Colisure ................ Colilert-18 ............. Tecta EC/TC.33 | ..................... ..................... ..................... 9223 B ......... ..................... ..................... ..................... 9223 B ......... | 9221 B.1, B.2 ......... 9223 B .................... 9223 B .................... 9223 B .................... 9221 F.1 ................. 9223 B .................... 9223 B .................... 9223 B .................... | 9221 B.1, B.2–06. 9223 B–04. 9223 B–04. 9223 B–04. 9221 F.1–06. 9223 B–04. 9223 B–04. 9223 B–04. |

40 CFR Ch. I (7–1–17 Edition)

450

Pt. 141, Subpt. C, App. A

ALTERNATIVE TESTING METHODS FOR CONTAMINANTS LISTED AT 40 CFR 143.4(b)

| Contaminant | Methodology | EPA method | ASTM 4 | SM 21st Edition 1 | SM 22nd Edition 28 | SM online 3 |
| --- | --- | --- | --- | --- | --- | --- |
| Aluminum ...................... Chloride ........................ Color ............................. Foaming Agents ........... Iron ................................ Manganese ................... Odor .............................. Silver ............................. Sulfate ........................... Total Dissolved Solids .. | Axially viewed inductively cou- pled plasma-atomic emis- sion spectrometry (AVICP– AES). Atomic Absorption; Direct ...... Atomic Absorption; Furnace ... Inductively Coupled Plasma ... Silver Nitrate Titration ............ Ion Chromatography .............. Potentiometric Titration .......... Visual Comparison ................. Methylene Blue Active Sub- stances (MBAS). Axially viewed inductively cou- pled plasma-atomic emis- sion spectrometry (AVICP– AES). Atomic Absorption; Direct ...... Atomic Absorption; Furnace ... Inductively Coupled Plasma ... Axially viewed inductively cou- pled plasma-atomic emis- sion spectrometry (AVICP– AES). Atomic Absorption; Direct ...... Atomic Absorption; Furnace ... Inductively Coupled Plasma ... Threshold Odor Test .............. Axially viewed inductively cou- pled plasma-atomic emis- sion spectrometry (AVICP– AES). Atomic Absorption; Direct ...... Atomic Absorption; Furnace ... Inductively Coupled Plasma ... Ion Chromatography .............. Gravimetric with ignition of residue. Gravimetric with drying of res- idue. Turbidimetric method ............. Automated methylthymol blue method. Total Dissolved Solids Dried at 180 deg C. | 200.5, Revision 4.2 2. ................................................. ................................................. ................................................. ................................................. ................................................. ................................................. ................................................. ................................................. 200.5, Revision 4.2 2. ................................................. ................................................. ................................................. 200.5, Revision 4.2 2. ................................................. ................................................. ................................................. ................................................. 200.5, Revision 4.2 2. ................................................. ................................................. ................................................. ................................................. ................................................. ................................................. ................................................. ................................................. ................................................. | ................................. ................................. ................................. D 512-04 B, 12 B .... D 4327-11 ............... ................................. ................................. ................................. ................................. ................................. ................................. ................................. ................................. ................................. ................................. ................................. ................................. ................................. D 4327-11 ............... ................................. ................................. D 516–07, 11 .......... ................................. ................................. | 3111 D .................... 3113 B ..................... 3120 B ..................... 4500-Cl¥ B ............. 4110 B ..................... 4500-Cl¥ D ............. 2120 B ..................... 5540 C .................... 3111 B ..................... 3113 B ..................... 3120 B ..................... 3111 B ..................... 3113 B ..................... 3120 B ..................... 2150 B ..................... 3111 B ..................... 3113 B ..................... 3120 B ..................... 4110 B ..................... 4500-SO4 2¥ C ........ 4500-SO4 2¥ D ........ 4500-SO4 2¥ E ........ 4500-SO4 2¥ F ........ 2540 C .................... | 3111 D. 3113 B ..................... 3120 B. 4500-Cl¥ B. 4110 B. 4500-Cl¥ D. 2120 B. 5540 C. 3111 B. 3113 B ..................... 3120 B. 3111 B. 3113 B ..................... 3120 B. 2150 B. 3111 B. 3113 B ..................... 3120 B. 4110 B. 4500-SO4 2¥ C ........ 4500-SO4 2¥ D ........ 4500-SO4 2¥ E ........ 4500-SO4 2¥ F ........ 2540 C. | 3113 B-04, B-10. 3113 B-04, B-10. 3113 B-04, B-10. 3113 B-04, B-10. 4500-SO4 2¥ C-97 4500-SO4 2¥ D-97 4500-SO4 2¥ E-97 4500-SO4 2¥ F-97 |

Zinc ...............................   Axially viewed inductively cou-

pled plasma-atomic emis- sion spectrometry (AVICP– AES).

Atomic Absorption; Direct As- piration.

200.5, Revision 4.2 2

Environmental Protection Agency

.................................................    .................................   3111 B .....................   3111 B.

451

Inductively Coupled Plasma ...   .................................................    .................................   3120 B .....................   3120 B.

1 Standard Methods for the Examination of Water and Wastewater, 21st edition (2005). Available from American Public Health Association, 800 I Street, NW., Washington, DC 20001– 3710.

2 EPA Method 200.5, Revision 4.2. ‘‘Determination of Trace Elements in Drinking Water by Axially Viewed Inductively Coupled Plasma-Atomic Emission Spectrometry.’’ 2003. EPA/600/R–

06/115

3 Standard Methods Online are available The year in which each method was approved by the Standard Methods Committee is designated by the last two digits in the method number. The methods listed are the only online versions that may be used.

4 Available from ASTM International, 100 Barr Harbor Drive, West Conshohocken, PA 19428–2959 or http://astm.org. The methods listed are the only alternative versions that may be

used.

5 Method D99–003, Revision 3.0. ‘‘Free Chlorine Species (HOCl¥ and OCl¥) by Test Strip,’’ November 21, 2003. Available from Industrial Test Systems, Inc., 1875 Langston St., Rock Hill, SC 29730.

6 Standard Methods for the Examination of Water and Wastewater, 20th edition (1998). Available from American Public Health Association, 800 I Street, NW., Washington, DC 20001–

3710.

7 Method ME355.01, Revision 1.0. ‘‘Determination of Cyanide in Drinking Water by GC/MS Headspace,’’ May 26, 2009. or from James Eaton, H & E Testing Laboratory, 221 State Street, Augusta, ME 04333. (207) 287–2727.

8 Systea Easy (1-Reagent). ‘‘Systea Easy (1-Reagent) Nitrate Method,’’ February 4, 2009. or from Systea Scientific, LLC., 900 Jorie Blvd., Suite 35, Oak

Brook, IL 60523.

9 EPA Method 524.3, Version 1.0. ‘‘Measurement of Purgeable Organic Compounds in Water by Capillary Column Gas Chromatography/Mass Spectrometry,’’ June 2009. EPA 815–B–09–

009. Available at the National Service Center for Environmental Publications  Search ‘‘815B09009’’.

10 Mitchell Method M5271, Revision 1.1. ‘‘Determination of Turbidity by Laser Nephelometry,’’ March 5, 2009. or from Leck Mitchell, PhD, PE, 656 Inde- pendence Valley Dr., Grand Junction, CO 81507.

11 Mitchell Method M5331, Revision 1.1. ‘‘Determination of Turbidity by LED Nephelometry,’’ March 5, 2009. Available or from Leck Mitchell, PhD, PE, 656 Inde-

pendence Valley Dr., Grand Junction, CO 81507.

12 Orion Method AQ4500, Revision 1.0. ‘‘Determination of Turbidity by LED Nephelometry,’’ May 8, 2009. Available or from Thermo Scientific, 166 Cummings Cen- ter, Beverly, MA 01915, .

13 Modified Colitag TM Method, ‘‘Modified Colitag TM Test Method for the Simultaneous Detection of E. coli and other Total Coliforms in Water (ATP D05–0035),’’ August 28, 2009. Available

or from CPI, International, 580 Skylane Boulevard, Santa Rosa, CA 95403.

14 EPA Method 557. ‘‘Determination of Haloacetic Acids, Bromate, and Dalapon in Drinking Water by Ion Chromatography Electrospray Ionization Tandem Mass Spectrometry (IC–ESI– MS/MS),’’ September 2009. EPA 815–B–09–012. Available at the National Service Center for Environmental Publications  Search ‘‘815B09012’’.

15 AMI Turbiwell, ‘‘Continuous Measurement of Turbidity Using a SWAN AMI Turbiwell Turbidimeter,’’ August 2009. or from Markus Bernasconi, SWAN

Analytische Instrumente AG, Studbachstrasse 13, CH–8340 Hinwil, Switzerland.

Pt. 141, Subpt. C, App. A

16 EPA Method 334.0. ‘‘Determination of Residual Chlorine in Drinking Water Using an On-line Chlorine Analyzer,’’ September 2009. EPA 815–B–09–013. Available at the National Service Center for Environmental Publications  Search ‘‘815B09013’’.

17 ChloroSense. ‘‘Measurement of Free and Total Chlorine in Drinking Water by Palintest ChloroSense,’’ August 2009. Available or from Palintest Ltd, 1455

Jamike Avenue (Suite 100), Erlanger, KY 41018.

18 EPA Method 302.0. ‘‘Determination of Bromate in Drinking Water using Two-Dimensional Ion Chromatography with Suppressed Conductivity Detection,’’ September 2009. EPA 815–B– 09–014. Available at the National Service Center for Environmental Publications  Search ‘‘815B09014’’.

19 EPA 415.3, Revision 1.2. ‘‘Determination of Total Organic Carbon and Specific UV Absorbance at 254 nm in Source Water and Drinking Water,’’ September 2009. EPA/600/R–09/122.

20 ReadycultMethod, ‘‘ReadycultColiforms 100 Presence/Absence Test for Detection and Identification of Coliform Bacteria and Escherichia coli in Finished Waters,’’ January, 2007. Version 1.1. Available from EMD Millipore (division of Merck KGaA, Darmstadt, Germany), 290 Concord Road, Billerica, MA 01821.

21 ChromocultMethod, ‘‘ChromocultColiform Agar Presence/Absence Membrane Filter Test Method for Detection and Identification of Coliform Bacteria and Escherichia coli in Finished

Waters,’’ November, 2000. Version 1.0. EMD Millipore (division of Merck KGaA, Darmstadt, Germany), 290 Concord Road, Billerica, MA 01821.

22 Hach Company Method, ‘‘Hach Company SPADNS 2 (Arsenic-free) Fluoride Method 10225—Spectrophotometric Measurement of Fluoride in Water and Wastewater,’’ January 2011. 5600 Lindbergh Drive, P.O. Box 389, Loveland, Colorado 80539..)

23 Hach Company. ‘‘Hach Company TNTplus TM 835/836 Nitrate Method 10206—Spectrophotometric Measurement of Nitrate in Water and Wastewater,’’ January 2011. 5600 Lindbergh Drive, P.O. Box 389, Loveland, Colorado 80539. (.)

24 EPA Method 525.3. ‘‘Determination of Semivolatile Organic Chemicals in Drinking Water by Solid Phase Extraction and Capillary Column Gas Chromatography/Mass Spectrometry (GC/ MS),’’ February 2012. EPA/600/R–12/010.

25 EPA Method 536. ‘‘Determination of Triazine Pesticides and their Degradates in Drinking Water by Liquid Chromatography Electrospray Ionization Tandem Mass Spectrometry (LC/ESI– MS/MS),’’ October 2007. EPA 815–B–07–002. Available at the National Service Center for Environmental Publications  Search ‘‘815B07002’’.

452

Pt. 141, Subpt. C, App. A

26 EPA Method 523. ‘‘Determination of Triazine Pesticides and their Degradates in Drinking Water by Gas Chromatography/Mass Spectrometry (GC/MS),’’ February 2011. EPA 815–R– 11–002. Available at the National Service Center for Environmental Publications  Search ‘‘815R11002’’.

27 EPA Method 1623.1. ‘‘Cryptosporidium and Giardia in Water by Filtration/IMS/FA,’’ 2012. EPA–816–R–12–001. Available at the National Service Center for Environmental Publications  Search ‘‘816R12001’’.

28 Standard Methods for the Examination of Water and Wastewater, 22nd edition (2012). Available from American Public Health Association, 800 I Street NW., Washington, DC 20001– 3710.

29 EPA Method 524.4, Version 1.0. ‘‘Measurement of Purgeable Organic Compounds in Water by Gas Chromatography/Mass Spectrometry using Nitrogen Purge Gas,’’ May 2013. EPA 815–R–13–002. Available at the National Service Center for Environmental Publications (). Search ‘‘815R13002’’.

30 Charm Sciences Inc. ‘‘Fast Phage Test Procedure. Presence/Absence for Coliphage in Ground Water with Same Day Positive Prediction’’. Version 009. November 2012. 659 Andover Street, Lawrence, MA 01843

31 Hach Company. ‘‘Hach Method 10260—Determination of Chlorinated Oxidants (Free and Total) in Water Using Disposable Planar Reagent-filled Cuvettes and Mesofluidic Channel Col- orimetry,’’ April 2013. 5600 Lindbergh Drive, P.O. Box 389, Loveland, CO 80539..)

32 ChlordioX Plus. ‘‘Chlorine Dioxide and Chlorite in Drinking Water by Amperometry using Disposable Sensors,’’ November 2013. Available from Palintest Ltd, Jamike Avenue (Suite 100), Erlanger, KY 41018.

33 Tecta EC/TC. ‘‘TechtaTM EC/TC Medium and TechtaTM Instrument: A Presence/Absence Method for the Simultaneous Detection of Total Coliforms and Escherichia coli (E. coli) in Drinking Water,’’ version 1.0, May 2014. Available from Veolia Water Solutions and Technologies, Suite 4697, Biosciences Complex, 116 Barrie Street, Kingston, Ontario, Canada, K7L 3N6. 34 Hach Company. ‘‘Hach Method 10241—Spectrophotometric Measurement of Free Chlorine (Cl2) in Finished Drinking Water,’’ November 2015. Revision 1.2. 5600 Lindbergh Drive, P.O.

Box 389, Loveland, CO 80539. (

35 Hach Company. ‘‘Hach Method 8026—Spectrophotometric Measurement of Copper in Finished Drinking Water,’’ December 2015. Revision 1.2. 5600 Lindbergh Drive, P.O. Box 389, Loveland, CO 80539..)

36 Hach Company. ‘‘Hach Method 10272—Spectrophotometric Measurement of Copper in Finished Drinking Water,’’ December 2015. Revision 1.2. 5600 Lindbergh Drive, P.O. Box 389, Loveland, CO 80539. (m.)

37 Hach Company. ‘‘Hach Method 10261—Total Organic Carbon in Finished Drinking Water by Catalyzed Ozone Hydroxyl Radical Oxidation Infrared Analysis,’’ December 2015. Revision

  - 5600 Lindbergh Drive, P.O. Box 389, Loveland, CO 80539. 38 Hach Company. ‘‘Hach Method 10267—Spectrophotometric Measurement of Total Organic Carbon (TOC) in Finished Drinking Water,’’ December 2015. Revision 1.2. 5600 Lindbergh Drive, P.O. Box 389, Loveland, CO 80539

39 Hach Company. ‘‘Hach Method 10258—Determination of Turbidity by 360Nephelometry,’’ January 2016. 5600 Lindbergh Drive, P.O. Box 389, Loveland, CO 80539.

.)

40 Nitrate Elimination Company, Inc. (NECi). ‘‘Method for Nitrate Reductase Nitrate-Nitrogen Analysis of Drinking Water,’’ February 2016. Superior Enzymes, Inc., 334 Hecla Street, Lake Linden, Michigan 49945.

41 Thermo Fisher. ‘‘Thermo Fisher Scientific Drinking Water Orthophosphate Method for Thermo Scientific Gallery Discrete Analyzer,’’ February 2016. Revision 5. Thermo Fisher Scientific, Ratastie 2, 01620 Vantaa, Finland.

42 Mitchell Method M5331, Revision 1.2. ‘‘Determination of Turbidity by LED or Laser Nephelometry,’’ February 2016. Available from Leck Mitchell, Ph.D., PE, 656 Independence Valley Dr., Grand Junction, CO 81507.

[74 FR 38353, Aug. 3, 2009, as amended at 74 FR 57914, Nov. 10, 2009; 74 FR 63069, Dec. 2, 2009; 75 FR 32299, June 8, 2010; 76 FR 37018, June

40 CFR Ch. I (7–1–17 Edition)

24, 2011; 77 FR 38527, June 28, 2012; 78 FR 32565, May 31, 2013; 78 FR 37463, June 21, 2013; 79 FR 35086, June 19, 2014; 79 FR 36428, June 27,

2014; 81 FR 46844, July 19, 2016]

#### Environmental Protection Agency	§ 141.33

Subpart D—Reporting and Recordkeeping

##### § 141.31   Reporting requirements.

    - Except where a shorter period is specified in this part, the supplier of water shall report to the State the re- sults of any test measurement or anal- ysis required by this part within (1) The first ten days following the month in which the result is received,  or  (2) the first ten days following the  end  of the required monitoring period as stip- ulated by the State, whichever of these is  shortest.

    - Except where a different reporting period is specified in this part, the sup- plier of water must report to the State within 48 hours the failure to comply with any national primary drinking water regulation (including failure to comply with monitoring requirements) set forth in this part.

    - The supplier of water is not re- quired to report analytical results to the State in cases where a State lab- oratory performs the analysis and re- ports the results to the State  office which would normally receive such no- tification from the  supplier.

    - The public water system, within 10 days of completing the public notifi- cation requirements under subpart Q of this part for the initial public notice and any repeat notices, must submit to the primacy agency a certification that it has fully complied with the public notification regulations. The public water system must include with this certification a representative copy of each type of notice distributed, pub- lished, posted, and made available to the persons served by  the  system  and to the media.

    - The water supply system shall submit to the State  within the  time stated in the request copies of any records required to be  maintained under § 141.33 hereof or copies of any documents then in existence which the State or the Administrator  is  entitled to inspect pursuant to the authority of section 1445 of the Safe Drinking Water Act or the equivalent provisions  of State  law.

[40 FR 59570, Dec. 24, 1975, as amended at 45

FR  57345,  Aug.  27,  1980;  65  FR  26022,  May  4,

2000]

##### § 141.32   [Reserved]

§ 141.33   Record maintenance.

Any owner or operator of a public water system subject to the provisions of this part shall retain on its premises or at a convenient location near its premises the following records:

- Records of microbiological anal- yses and turbidity analyses made pur- suant to this part shall be kept for not less than 5 years. Records of chemical analyses made pursuant to this part shall be kept for not less than 10 years. Actual laboratory reports may be kept, or data may be transferred to tabular summaries, provided that the following information is included:

  - The date, place, and time of sam- pling, and the name of the person who collected the sample;

  - Identification of the sample as to whether it was a routine distribution system sample, check sample, raw or process water sample or other special purpose sample;

  - Date of analysis;

  - Laboratory and person responsible for performing analysis;

  - The analytical technique/method used; and

  - The results of the analysis.

- Records of action taken by the system to correct violations of primary drinking water regulations shall be kept for a period not less than 3 years after the last action taken with respect to the particular violation involved.

- Copies of any written reports, summaries or communications relating to sanitary surveys of the system con- ducted by the system itself, by a pri- vate consultant, or by  any  local,  State or Federal agency, shall be kept for a period not less than 10 years after com- pletion of the sanitary survey involved.

- Records concerning a variance or exemption granted to the system  shall be kept for a period ending not less than 5 years following the expiration of such variance or exemption.

- Copies of public notices issued pursuant to subpart Q of this part and certifications  made  to  the  primacy agency pursuant to § 141.31  must  be kept  for  three  years  after  issuance.

- Copies of monitoring plans devel- oped pursuant to this part shall be kept for the same period of time as the

#### § 141.34

records of analyses taken  under  the plan are required to be kept under paragraph (a) of this section, except as specified elsewhere in this part.

[40 FR 59570, Dec. 24, 1975, as amended at 65

FR 26022, May 4, 2000; 71 FR 478, Jan. 4, 2006]

##### § 141.34   [Reserved]

§ 141.35   Reporting	for	unregulated contaminant monitoring results.

- General applicability. This section applies to any owner or operator of a public water system (PWS) required to monitor for unregulated contaminants under § 141.40(a); such owner or oper- ator is referred to as ‘‘you.’’ This sec- tion specifies the information that must be reported to EPA prior to the commencement of monitoring and de- scribes the process for reporting moni- toring results to EPA. For the purposes of this section, PWS ‘‘population served’’ is the retail population served directly by the PWS as reported to the Federal Safe Drinking Water Informa- tion System (SDWIS/Fed); wholesale or consecutive populations are not in- cluded. For purposes of this section, the term ‘‘finished’’ means water that is introduced into the distribution sys- tem of a PWS and is intended for dis- tribution and consumption without further treatment, except the treat- ment necessary to maintain water quality in the distribution system (e.g., booster disinfection, addition of corro- sion control chemicals). For purposes of this section, the term ‘‘State’’ refers to the State or Tribal government enti- ty that has jurisdiction over your PWS even if that government does not have primary enforcement responsibility for PWSs under  the  Safe Drinking  Water Act. For purposes of this section,  the term ‘‘PWS Official’’ refers to the per- son at your PWS who is able to func- tion as the official spokesperson for the system’s Unregulated Contaminant Monitoring Regulation (UCMR) activi- ties; and the term ‘‘PWS Technical Contact’’ refers to the person at your PWS who is responsible for the tech- nical aspects of your UCMR activities, such as details concerning sampling and reporting.

- Reporting by all systems. You must meet   the   reporting   requirements   of

#### 40 CFR Ch. I (7–1–17 Edition)

this paragraph if you meet the applica- bility criteria in § 141.40(a)(1) and (2).

  - Where to submit UCMR reporting re- quirement information. Some of your re- porting requirements are to be fulfilled electronically and others by mail. In- formation that must  be  submitted using EPA’s electronic data reporting system must be submitted through: .	Docu- mentation that is required to be mailed can be submitted either: To UCMR Sampling Coordinator, USEPA, Tech- nical Support Center, 26 West Martin Luther King Drive (MS  140),  Cin- cinnati, OH 45268; or by email at UCMRlSamplinglCoordinator@epa.gov. In addition, you must notify the public of the availability of unregulated con- taminant monitoring data as  provided in subpart  Q (Public Notification)  of this part (40 CFR 141.207). Community Water Systems that detect unregulated contaminants under  this monitoring must also address such detections as part of their Consumer Confidence Re- ports, as provided in subpart O of this part (40 CFR 141.151).

  - Contacting EPA if your system does not meet applicability criteria or has a status change. If you have received a letter from EPA or your State con- cerning your required monitoring and your system does not meet the applica- bility  criteria  for  UCMR  established  in

§ 141.40(a)(1) or (2), or if a change occurs at your system that may affect your requirements under UCMR as  defined in § 141.40(a)(3) through (5), you must mail or email a letter to EPA, as speci- fied in paragraph (b)(1) of this section. The letter must be from your PWS Of- ficial and must include your PWS Iden- tification (PWSID) Code along with an explanation as to why the UCMR re- quirements are not applicable to your PWS, or have changed for your PWS, along with the appropriate contact in- formation. EPA will make an applica- bility determination based on your let- ter and in consultation with the State when necessary. You are subject to UCMR requirements unless and until you receive a letter from EPA agreeing that you do not meet the applicability criteria.

- Reporting by large systems. If you serve  a  population  of  more  than  10,000

#### Environmental Protection Agency	§ 141.35

people, and meet the applicability cri- teria in § 141.40(a)(2)(i), you must meet the reporting requirements in para- graphs (c)(1) through (8) of this section.

  - Contact and zip code information. You must provide contact information by December 31, 2017, and provide up- dates within 30 days if this information changes. The contact information must be submitted using EPA’s electronic data reporting system, as specified in paragraph (b)(1) of this section, and in- clude the name, affiliation, mailing ad- dress, phone number, and email address for your PWS Technical Contact and your PWS Official. In addition, as a one-time reporting requirement, you must report the U.S. Postal Service Zip Code(s) for all areas being served water by your PWS.

  - Sampling location and inventory in- formation. You must provide your sam- pling location(s) and inventory infor- mation by December 31, 2017, using EPA’s electronic data reporting sys- tem. You must submit, verify or up- date the following information for each sampling location, or for each approved representative sampling location (as specified in paragraph (c)(3) of this sec- tion regarding representative sampling locations): PWSID Code; PWS Name; PWS Facility Identification Code; PWS Facility Name; PWS Facility  Type; Water Source Type; Sampling Point Identification Code; Sampling Point Name; and Sampling Point Type Code; (as defined in Table 1 of paragraph (e) of this section). If this information changes, you must report updates, in- cluding new sources and sampling loca- tions that are put in use before or dur- ing the PWS’ UCMR  sampling  period, to EPA’s electronic data reporting sys- tem within 30 days of the change.

  - Proposed ground water representa- tive sampling locations. Some systems that use ground water as a source and have multiple entry points to the dis- tribution system (EPTDSs) may pro- pose monitoring  at  representative entry point(s), rather than monitor at every EPTDS, as follows:

    - Qualifications. Large PWSs that have EPA- or State-approved alternate EPTDS sampling locations from a pre- vious UCMR cycle, or as provided for under  § 141.23(a)(1),  § 141.24(f)(1),  or

§ 141.24(h)(1), may submit a copy of doc-

umentation from their  State  or  EPA that approves their alternative sam- pling plan for EPTDSs. PWSs that do not have an approved alternative EPTDS sampling plan may submit a proposal to sample at representative EPTDS(s) rather than at each indi- vidual EPTDS if: They use ground water as a source; all of their well sources have either the same  treat- ment or no treatment; and they have multiple EPTDSs  from  the  same source, such as an aquifer. You must submit a copy of the existing alternate EPTDS sampling plan or your rep- resentative well proposal, as appro- priate, April 19, 2017, as specified in paragraph (b)(1) of this section.

    - Demonstration. If you are submit- ting a proposal to sample at represent- ative EPTDS(s) rather than at each in- dividual EPTDS, you must dem- onstrate that any EPTDS that you se- lect as representative of the ground water you supply from multiple wells is associated with a well that draws from the same aquifer as the wells it will represent. The proposed well must be representative of the highest annual volume producing and most consist- ently active wells in the representative array. If that representative well is not in use at the scheduled sampling time, you must select and sample an alter- native representative well. You must submit the following information for each proposed representative sampling location: PWSID Code; PWS Name; PWS Facility Identification Code; PWS Facility Name; PWS Facility Type; Sampling Point Identification Code; and Sampling Point Name (as defined in Table 1, paragraph (e) of this sec- tion). You must also include docu- mentation to support your proposal that the specified wells are representa- tive of other wells. This documentation can include system-maintained well logs or construction drawings indi- cating that the representative well(s) is/are at a representative depth, and de- tails of well casings and grouting; data demonstrating relative homogeneity of water quality constituents (e.g., pH, dissolved oxygen, conductivity, iron, manganese) in samples drawn from each well; and data showing that your wells are located in a limited geo- graphic area (e.g., all wells within a 0.5

#### § 141.35

mile radius) and/or, if available, the hydrogeologic data indicating the  time of travel separating the representative well from each  of  the  individual  wells it represents (e.g., all wells within a five-year time of travel delineation). Your proposal must  be sent in writing to EPA, as specified in paragraph (b)(1) of this  section.  You  must  also  provide a copy of this information to the State, unless otherwise directed by the State. Information about the actual or poten- tial occurrence or non-occurrence of contaminants in  an  individual  well,  or a well’s vulnerability to contamina- tion, must not be used as a basis for se- lecting a representative well.

    - Approval. EPA or the State (as specified in the Partnership Agreement reached between the State and EPA) will review your proposal, coordinate any necessary changes  with you, and approve the final list of EPTDSs where you will be required to monitor. Your plan will not be final until you receive written approval from EPA or the State.

  - Contacting EPA if your PWS has not been notified of requirements. If you be- lieve you are subject to UCMR require- ments, as defined in § 141.40(a)(1) and (2)(i), and you have not  been  notified by either EPA or your State  by  April 19, 2017, you must send a letter to EPA, as specified in paragraph (b)(1) of this section. The letter must be from your PWS Official and must include an ex- planation as to why the UCMR require- ments are applicable to your  system along with the appropriate contact in- formation. A  copy  of  the  letter  must also be submitted to the State, as di- rected by the State. EPA will make an applicability determination based  on your  letter,  and  in  consultation  with the State when necessary, and will no- tify you regarding your  applicability status and required sampling schedule. However, if your PWS meets the appli- cability	criteria	specified	in

§ 141.40(a)(2)(i), you are subject to the UCMR monitoring and reporting re- quirements, regardless of whether you have been notified  by  the  State  or EPA.

  - Notifying EPA if your PWS cannot sample according to schedule—

    - General rescheduling notification re- quirements.  Large  systems  may  change

#### 40 CFR Ch. I (7–1–17 Edition)

their monitoring schedules up to De- cember 31, 2017, using EPA’s electronic data reporting system, as specified in paragraph (b)(1) of this section. After this date has passed, if your PWS can- not sample according to your assigned sampling schedule (e.g., because of budget constraints, or if a sampling lo- cation will be closed during the sched- uled month of monitoring), you must mail or email a letter to EPA, as speci- fied in paragraph (b)(1) of this section, prior to the scheduled sampling date. You must include  an  explanation  of why the samples cannot be taken ac- cording to the assigned schedule, and you must provide the alternative schedule you are requesting. You must not reschedule monitoring specifically to avoid sample collection during a suspected vulnerable period. You are subject to your assigned UCMR sam- pling schedule or the schedule that you revised on or before December 31, 2017, unless and until you receive a letter from EPA specifying a new schedule.

    - Exceptions to the rescheduling noti- fication requirements. For ground water sampling, if the second round of sam- pling will be completed five to seven months after the first  sampling  event, as       specified       in       Table       2       of

§ 141.40(a)(4)(i)(B), no notification to EPA is required. If any ground water sampling location will be non-oper- ational for more than one month before and one month after the month  in which the second sampling event is scheduled (i.e., it is not possible for you to sample within the five to seven month window), you must  notify  EPA, as specified in paragraph (b)(1) of this section, explaining why the schedule cannot be met. You must comply with any modified  schedule  provided  by EPA.

  - Reporting monitoring results. For UCMR samples, you must  report  all data elements specified in Table 1 of paragraph (e) of this section, using EPA’s electronic data reporting sys- tem. You  also  must  report  any changes, relative to what is currently posted, made to data elements 1 through 9 to EPA in writing,  explain- ing the nature and purpose of the pro- posed change, as specified in paragraph (b)(1) of this section.

#### Environmental Protection Agency	§ 141.35

    - Electronic reporting system. You are responsible for ensuring that the lab- oratory conducting the analysis of your unregulated contaminant moni- toring samples (your laboratory) posts the analytical results to EPA’s elec- tronic reporting system. You are also responsible for reviewing, approving, and submitting those results to EPA.

    - Reporting schedule. You must en- sure that your laboratory  posts  the data to EPA’s electronic data reporting system within 120 days from the sam- ple collection date (sample collection must occur as specified in § 141.40(a)(4)). You have 60 days from when the lab- oratory posts the data in EPA’s elec- tronic data reporting system to review, approve, and submit the data to the State and EPA, at the Web address specified in paragraph (b)(1) of this sec- tion. If you do not electronically ap- prove and submit the  laboratory  data to EPA within 60 days of the labora- tory’s posting data to EPA’s electronic reporting system, the data will be con- sidered approved by you and available for State and EPA review.

  - Only one set of results accepted.  If you report more than one set of valid results for the same sampling location and the same sampling event (for ex- ample, because  you  have   had   more than one laboratory analyze replicate samples collected under § 141.40(a)(5), or because you have collected multiple samples during a  single  monitoring event at the  same  sampling  location), EPA will use the highest of  the  re- ported  values  as  the  official  result.

  - No reporting of previously collected data. You cannot report previously col- lected data to meet the testing and re- porting requirements for the contami- nants listed in § 141.40(a)(3). All anal- yses must be performed by laboratories approved by EPA to perform UCMR analyses using the analytical methods specified in Table 1 of § 141.40(a)(3) and using   samples   collected   according   to

§ 141.40(a)(4). Such requirements pre- clude	the	possibility	of ‘‘grandfathering’’ previously collected data.

- Reporting by small systems. If you serve a population of 10,000 or fewer people, and you are notified that you have been selected for UCMR moni- toring,     your     reporting     requirements

will be specified within the materials that EPA sends you, including a re- quest for contact information, and a request for information associated with the sampling kit.

- Contact and zip code information. EPA will send you a notice requesting contact information for key  individ- uals at your system, including name, affiliation, mailing address, phone number and email address. These indi- viduals include your PWS Technical Contact  and  your  PWS  Official.  You are required to provide this contact in- formation within 90 days of receiving the notice from EPA as specified in paragraph (b)(1) of this section. If this contact information changes, you also must provide updates within 30 days of the change, as specified in paragraph (b)(1) of this section. In addition, as a one-time reporting requirement, you must report the U.S. Postal Service Zip Code(s) for all areas being served water by your PWS.

- Reporting  sampling  information. You must provide your sampling loca- tion(s) by December 31, 2017, using EPA’s  electronic  data  reporting  sys- tem, as specified in paragraph (b)(1) of this  section.  If  this  information changes, you must report updates, in- cluding new sources and sampling loca- tions that are put in use  before  or  dur- ing  the  PWS’  UCMR   sampling   period, to EPA’s electronic data reporting sys- tem within 30 days of the change, as specified in paragraph (b)(1) of this sec- tion. You must record all data  ele- ments listed in Table 1 of paragraph (e) of this section on each sample form and sample bottle, as appropriate,  provided to you by the UCMR Sampling Coordi- nator. You must send  this  information as specified in the instructions of your sampling kit,  which  will  include  the due date and return address. You must report any changes made in data ele- ments 1 through 9 by emailing an ex- planation of the nature and purpose  of the proposed change to EPA, as speci- fied  in  paragraph  (b)(1)  of  this  section.

- Data elements. Table 1 defines the data elements that must be provided for  UCMR  monitoring.

#### § 141.35

40 CFR Ch. I (7–1–17 Edition)

TABLE 1—UNREGULATED CONTAMINANT MONITORING REPORTING REQUIREMENTS

Data element	Definition

- Public Water System Identi- fication (PWSID) Code.

The code used to identify each PWS. The code begins with the standard 2-character postal State abbreviation or Region code; the remaining 7 numbers are unique to each PWS in the State. The same identification code must be used to represent the PWS identification for all current and future UCMR monitoring.

- Public Water System Name	Unique name, assigned once by the PWS.

- Public Water System Facility Identification Code.

- Public Water System Facility Name.

- Public Water System Facility Type.

An identification code established by the State or, at the State’s discretion, by the PWS, fol- lowing the format of a 5-digit number unique within each PWS for each applicable facility (i.e., for each source of water, treatment plant, distribution system, or any other facility asso- ciated with water treatment or delivery). The same identification code must be used to rep- resent the facility for all current and future UCMR monitoring.

Unique name, assigned once by the PWS, for every facility ID (e.g., Treatment Plant).

That code that identifies that type of facility as either: CC = consecutive connection.

DS = distribution system. IN = source water influent. SS = sampling station.

TP = treatment plant. OT = other.

- Water Source Type ..............   The type of source water that supplies a water system facility. Systems must report one of the following codes for each sampling location:

SW = surface water (to be reported for water facilities that are served entirely by a surface water source during the twelve-month period).

GW = ground water (to be reported for water facilities that are served entirely by a ground water source during the twelve-month period).

GU = ground water under the direct influence of surface water (to be reported for water facili- ties that are served all or in part by ground water under the direct influence of surface water at any time during the twelve-month sampling period), and are not served at all by surface water during this period.

MX = mixed water (to be reported for water facilities that are served by a mix of surface water, ground water and/or ground water under the direct influence of surface water during the twelve-month period).

- Sampling Point Identification Code.

An identification code established by the State, or at the State’s discretion, by the PWS, that uniquely identifies each sampling point. Each sampling code must be unique within each ap- plicable facility, for each applicable sampling location (i.e., entry point to the distribution sys- tem, source water influent or distribution system sample at maximum residence time). The same identification code must be used to represent the sampling location for all current and future UCMR monitoring.

- Sampling Point Name  ..........   Unique sample point name, assigned once by the PWS, for every sample point ID (e.g., Entry Point).

- Sampling Point Type Code ..   A code that identifies the location of the sampling point as either:

SR = source water taken from plant influent; untreated water entering the water treatment plant (i.e., a location prior to any treatment).

EP = entry point to the distribution system. DS = distribution system sample.

- Disinfectant Type ................   All of the disinfectants/oxidants that have been added prior to the entry point to the distribution system. Please select all that apply:

PEMB = Permanganate. HPXB = Hydrogen peroxide. CLGA = Gaseous chlorine.

CLOF = Offsite Generated Hypochlorite (stored as a liquid form). CLON = Onsite Generated Hypochlorite.

CAGC = Chloramine (formed with gaseous chlorine). CAOF = Chloramine (formed with offsite hypochlorite). CAON = Chloramine (formed with onsite hypochlorite). CLDB = Chlorine dioxide.

OZON = Ozone.

ULVL = Ultraviolet light.

OTHD = All other types of disinfectant/oxidant. NODU = No disinfectant/oxidant used.

- Treatment Information ........   Treatment information associated with the sample point. Please select all that apply:

CON = Conventional (non-softening, consisting of at least coagulation/sedimentation basins and filtration).

SFN = Softening.

RBF = River bank filtration. PSD = Pre-sedimentation. INF = In-line filtration.

DFL = Direct filtration. SSF = Slow sand filtration.

BIO = Biological filtration (operated with an intention of maintaining biological activity within fil- ter).

UTR = Unfiltered treatment for surface water source.

#### Environmental Protection Agency	§ 141.35

TABLE 1—UNREGULATED CONTAMINANT MONITORING REPORTING REQUIREMENTS—Continued

Data element	Definition

GWD = Groundwater system with disinfection only. PAC = Application of powder activated carbon.

GAC = Granular activated carbon adsorption (not part of filters in CON, SCO, INF, DFL, or SSF).

AIR = Air stripping (packed towers, diffused gas contactors).

POB = Pre-oxidation with chlorine (applied before coagulation for CON or SFN plants or be- fore filtration for other filtration plants).

MFL = Membrane filtration. IEX = Ionic exchange.

DAF = Dissolved air floatation.

CWL = Clear well/finished water storage without aeration. CWA = Clear well/finished water storage with aeration.

ADS = Aeration in distribution system (localized treatment). OTH = All other types of treatment.

NTU = No treatment used. DKN = Do not know.

- Disinfectant Residual Type     Disinfectant residual type in the distribution system for each HAA sample.

CL2 = Chlorine (i.e., originating from addition of free chlorine only). CLO2 = chlorine dioxide.

CLM = Chloramines (originating from with addition of chlorine and ammonia or pre-formed chloramines).

CAC = Chlorine and chloramines (if being mixed from chlorinated and chloroaminated water). NOD = No disinfectant residual.

- Sample Collection Date ......   The  date  the  sample  is  collected,  reported  as  4-digit  year,  2-digit  month,  and  2-digit  day (YYYY/MM/DD).

- Sample Identification Code An alphanumeric value up to 30 characters assigned by the laboratory to uniquely identify con- tainers, or groups of containers, containing water samples collected at the same sampling location for the same sampling date.

- Contaminant .......................   The unregulated contaminant for which the sample is being analyzed.

- Analytical Method Code .....   The identification code of the analytical method used.

- Extraction Batch Identifica- tion Code.

Laboratory assigned extraction batch ID. Must be unique for each extraction batch within the laboratory for each method. For CCC samples report the Analysis Batch Identification Code as the value for this field. For methods without an extraction batch, leave this field null.

- Extraction Date ...................   Date for the start of the extraction batch (YYYY/MM/DD). For methods without an extraction batch, leave this field null.

- Analysis Batch Identification Code.

Laboratory assigned analysis batch ID. Must be unique for each analysis batch within the lab- oratory for each method.

- Analysis Date  .....................   Date for the start of the analysis batch (YYYY/MM/DD).

- Sample Analysis Type ........   The type of sample collected and/or prepared, as well as the fortification level. Permitted val- ues include:

CF = concentration fortified; the concentration of a known contaminant added to a field sample reported with sample analysis types LFSM, LFSMD, LFB, CCC and QCS.

CCC = continuing calibration check; a calibration standard containing the contaminant, the in- ternal standard, and surrogate analyzed to verify the existing calibration for those contami- nants.

FS = field sample; sample collected and submitted for analysis under this rule.

IS = internal standard; a standard that measures the relative response of contaminants.

LFB = laboratory fortified blank; an aliquot of reagent water fortified with known quantities of the contaminants and all preservation compounds.

LRB = laboratory reagent blank; an aliquot of reagent water treated exactly as a field sample, including the addition of preservatives, internal standards, and surrogates to determine if interferences are present in the laboratory, reagents, or other equipment.

LFSM = laboratory fortified sample matrix; a UCMR field sample with a known amount of the contaminant of interest and all preservation compounds added.

LFSMD = laboratory fortified sample matrix duplicate; duplicate of the laboratory fortified sam- ple matrix.

QCS = quality control sample; a sample prepared with a source external to the one used for initial calibration and CCC. The QCS is used to check calibration standard integrity.

QHS = quality HAA sample; HAA sample collected and submitted for quality control purposes. SUR = surrogate standard; a standard that assesses method performance for each extraction.

- Analytical Results—Sign ....   A value indicating whether the sample analysis result was:

(<) ‘‘less than’’ means the contaminant was not detected, or was detected at a level below the Minimum Reporting Level.

(=) ‘‘equal to’’ means the contaminant was detected at the level reported in ‘‘Analytical Re- sult— Measured Value.’’

- Analytical Result—Meas- ured Value.

The actual numeric value of the analytical results for: Field samples; laboratory fortified matrix samples; laboratory fortified sample matrix duplicates; and concentration fortified.

- Additional Value ................. Represents the true value or the fortified concentration for spiked samples for QC Sample Analysis Types (CCC, EQC, LFB, LFSM and LFSMD). For Sample Analysis Type FS and LRB and for IS and surrogate QC Contaminants, leave this field null.

#### § 141.35

40 CFR Ch. I (7–1–17 Edition)

TABLE 1—UNREGULATED CONTAMINANT MONITORING REPORTING REQUIREMENTS—Continued

| Data element | Definition |
| --- | --- |
| Laboratory Identification Code. Sample Event Code ........... Bloom Occurrence .............. Cyanotoxin Occurrence ...... Indicator of Possible Bloom—Treatment. Indicator of Possible Bloom—Source Water Qual- ity Parameters. | The code, assigned by EPA, used to identify each laboratory. The code begins with the stand- ard two-character State postal abbreviation; the remaining five numbers are unique to each laboratory in the State. A code assigned by the PWS for each sample event. This will associate samples with the PWS monitoring plan to allow EPA to track compliance and completeness. Systems must assign the following codes: SEC1, SEC2, SEC3, SEC4, SEC5, SEC6, SEC7 and SEC8—represent samples collected to meet UCMR Assessment Monitoring requirements for cyanotoxins; where ‘‘SEC1’’ rep- resents the first sampling period, ‘‘SEC2’’ the second period and so forth, for all eight sam- pling events. SEA1, SEA2, SEA3 and SEA4—represent samples collected to meet UCMR Assessment Monitoring requirements for the additional contaminants; where ‘‘SEA1’’ and ‘‘SEA2’’ rep- resent the first and second sampling period for all water types; and ‘‘SEA3’’ and ‘‘SEA4’’ represent the third and fourth sampling period for SW and GU sources only. A yes or no answer provided by the PWS for each cyanotoxin sample event. Question: Preceding the finished water sample collection, did you observe an algal bloom in your source waters near the intake? YES = if yes, select all the YESs that apply: YD = yes, on the day the UCMR cyanotoxin sample was collected. YW = yes, between the day the sample was taken and the past week. YM = yes, between the past week and past month. YY = yes, between the past month and past year. YP = yes, prior to the past year. NO = have never seen a bloom. A yes or no answer provided by the PWS for each cyanotoxin sample event. Question: Preceding the finished water sample collection, were cyanotoxins ever detected in your source waters near the intake and prior to any treatment (based on sampling by you or another party)? YES = if yes, select all the YESs that apply: YD = yes, on the day the UCMR cyanotoxin sample was collected. YW = yes, between the day the sample was taken and the past week. YM = yes, between the past week and past month. YY = yes, between the past month and past year. YP = yes, prior to the past year. NO = have never detected cyanotoxins in source water. NS = unaware of any source water cyanotoxin sampling. Select all that apply (i.e., all that were detected) if you answered YES to detecting cyanotoxins in source water: MIC = Microcystins. CYL = Cylindrospermopsin. ANA = Anatoxin-A. SAX = Saxitoxins. OTH = Other. DK = do not know. A yes or no answer provided by the PWS for each cyanotoxin sample event. Question: Preceding the finished water sample collection, did you notice any changes in your treatment system operation and/or treated water quality that may indicate a bloom in the source water? YES = if yes, select all that apply: DFR = Decrease in filter runtimes. ITF = Increase in turbidity in filtered water. ICD = Need for increased coagulant dose. TOI = Increase in taste and odor issues in finished water. IOD = Need for increase in oxidant/disinfectant dose. IDB = Increase in TTHM/HAA5 in finished water. OTH = Describe other changes. NO = no changes. A yes or no answer provided by the PWS for each cyanotoxin sample event. Question: Preceding the finished water sample collection, did you observe any notable changes in source water quality parameters (if measured)? YES = if yes, select all that apply to the source water: ITP = Increase in water temperature. ITU = Increase in turbidity. IAL = Increase in alkalinity. ITO = Increase in total organic carbon. ICD = Increase in chlorine demand. IPH = Increase in pH. ICA = Increase in chlorophyll a. IPY = Increase in phycocyanin. INU = Increase in nutrients (example: nitrogen or phosphorus). OTH = Describe other changes. NO = no changes observed. |

#### Environmental Protection Agency	§ 141.40

[72 FR 389, Jan. 4, 2007, as amended at 77 FR 26096, May 2, 2012; 81 FR 92684, Dec. 20, 2016]

# Subpart E—Special Regulations, Including Monitoring Regula- tions and Prohibition on Lead Use

##### § 141.40 Monitoring requirements for unregulated contaminants.

- General applicability. This section specifies  the  monitoring  and  quality control requirements that must be fol- lowed if you own or operate a public water system (PWS) that is subject to the   Unregulated   Contaminant   Moni- toring Regulation (UCMR), as specified in paragraphs (a)(1) and (2) of this sec- tion. In addition, this section specifies the UCMR requirements for State and Tribal participation. For the purposes of    this    section,    PWS    ‘‘population served,’’    ‘‘State,’’    ’’    PWS    Official,’’ ‘‘PWS  Technical  Contact,’’  and  ‘‘fin- ished   water’’   apply   as   defined   in

§ 141.35(a). The determination of wheth- er a PWS is required to monitor under this rule is based on the type of system (e.g., community water system, non- transient non-community water sys- tem, etc.), and its retail population, as indicated by SDWIS/Fed on December 31, 2015.

  - Applicability to transient non-com- munity systems. If you own or operate a transient non-community water sys- tem, you are not subject to monitoring requirements in this section.

  - Applicability to community water systems and non-transient  non-commu- nity water systems—(i) Large systems. If you own or operate a retail PWS (other than a transient non-community sys- tem) that serves more than 10,000 peo- ple, you must monitor according to the specifications in  this  paragraph (a)(2)(i). If you believe that your appli- cability status  is  different  than  EPA has specified in the notification letter that you received, or if you are subject to UCMR requirements and you have not been notified  by  either  EPA  or your State, you must report to EPA, as specified in § 141.35(b)(2) or (c)(4).

    - Assessment monitoring. You must monitor for the contaminants on List 1, per Table 1, UCMR Contaminant List, in paragraph (a)(3) of this section. If you serve a retail population of more

than 10,000 people, you are required to perform this monitoring regardless of whether you have been notified by the State   or   EPA.

    - Screening Survey. You must mon- itor for the unregulated contaminants on List 2 (Screening Survey) of Table 1, as specified in paragraph (a)(3) of this section, if your system serves 10,001 to 100,000 people and you are notified by EPA or your State that you are part of the State Monitoring Plan for Screen- ing Survey testing. If your system serves more than 100,000 people, you are required  to conduct  this Screening Survey testing regardless  of  whether you have been notified by the State or EPA.

    - Pre-Screen Testing. You must mon- itor  for  the  unregulated  contaminants on List 3 of Table 1, in paragraph (a)(3) of  this  section,  if   notified   by   your State or EPA that you are part of the Pre-Screen    Testing.

- Small systems. Small PWSs, as de- fined in this paragraph, will not be se- lected to monitor for any more than one of the three monitoring lists pro- vided in  Table  1,  UCMR  Contaminant List, in paragraph (a)(3) of this section. EPA will provide sample containers, provide pre-paid air bills for shipping the sampling materials, conduct the laboratory analysis, and report and re- view monitoring results for all small systems selected to conduct moni- toring under paragraphs (a)(2)(ii)(A) through (C) of this section. If you own or operate a PWS that serves 10,000 or fewer people you must monitor as fol- lows:

  - Assessment monitoring. You must monitor for the contaminants on List 1 per Table 1, in paragraph (a)(3) of this section, if you are  notified  by  your State or EPA that you are part of the State Monitoring Plan for Assessment Monitoring.

  - Screening Survey. You must mon- itor for the unregulated contaminants on List 2 of Table 1, in paragraph (a)(3) of this section, if  notified  by  your State or EPA that you are part of the State Monitoring Plan for the Screen- ing  Survey.

§ 141.40

  - Pre-screen testing. You must mon- itor for the contaminants on List 3 of Table 1, in paragraph (a)(3) of this sec- tion if you are  notified  by  your  State or  EPA  that  you  are  part  of  the  State

#### 40 CFR Ch. I (7–1–17 Edition)

Monitoring  Plan  for  Pre-Screen  Test- ing.

  - Analytes to be monitored. Lists 1, 2, and 3 contaminants are provided in the following  table:

TABLE 1—UCMR CONTAMINANT LIST

| 1—Contaminant | 2—CAS Registry No. | 3—Analytical methods a | 4—Minimum reporting level b | 5—Sampling location c | 6—Period during which monitoring to be completed |
| --- | --- | --- | --- | --- | --- |

List 1: Assessment Monitoring Cyanotoxin Chemical Contaminants

| ‘‘total microcystin’’ ....... anatoxin-a ................... cylindrospermopsin ..... microcystin-LA ............ microcystin-LF ............ microcystin-LR ............ microcystin-LY ............ microcystin-RR ........... microcystin-YR ............ nodularin ..................... | N/A ........... 64285–06– 9. 143545– 90–8. 96180–79– 9. 154037– 70–4. 101043– 37–2. 123304– 10–9. 111755– 37–4. 101064– 48–6. 118399– 22–7. | EPA 546 ................ EPA 545 ................ EPA 545 ................ EPA 544 ................ EPA 544 ................ EPA 544 ................ EPA 544 ................ EPA 544 ................ EPA 544 ................ EPA 544 ................ | 0.3 g/L ........ 0.03 g/L ...... 0.09 g/L ...... 0.008 g/L .... 0.006 g/L .... 0.02 g/L ...... 0.009 g/L .... 0.006 g/L .... 0.02 g/L ...... 0.005 g/L .... | EPTDS .............. EPTDS .............. EPTDS .............. EPTDS .............. EPTDS .............. EPTDS .............. EPTDS .............. EPTDS .............. EPTDS .............. EPTDS .............. | 3/1/2018–11/30/2020. 3/1/2018–11/30/2020. 3/1/2018–11/30/2020. 3/1/2018–11/30/2020. 3/1/2018–11/30/2020. 3/1/2018–11/30/2020. 3/1/2018–11/30/2020. 3/1/2018–11/30/2020. 3/1/2018–11/30/2020. 3/1/2018–11/30/2020. |
| --- | --- | --- | --- | --- | --- |

List 1: Assessment Monitoring Additional Chemical Contaminants

Metals

| germanium .................. manganese ................. | 7440–56–4 7439–96–5 | EPA 200.8, ASTM D5673–10, SM 3125. EPA 200.8, ASTM D5673–10, SM 3125. | 0.3 g/L ........ 0.4 g/L ........ | EPTDS .............. EPTDS .............. | 1/1/2018–12/31/2020. 1/1/2018–12/31/2020. |
| --- | --- | --- | --- | --- | --- |

Pesticides and a Pesticide Manufacturing Byproduct

| alpha- hexachlorocyclohex- ane. chlorpyrifos ................. dimethipin ................... ethoprop ...................... oxyfluorfen .................. profenofos ................... tebuconazole .............. total permethrin (cis- & trans-). tribufos ........................ | 319–84–6 2921–88–2 55290–64– 7. 13194–48– 4. 42874–03– 3. 41198–08– 7. 107534– 96–3. 52645–53– 1. 78–48–8 ... | EPA 525.3 ............. EPA 525.3 ............. EPA 525.3 ............. EPA 525.3 ............. EPA 525.3 ............. EPA 525.3 ............. EPA 525.3 ............. EPA 525.3 ............. EPA 525.3 ............. | 0.01 g/L ...... 0.03 g/L ...... 0.2 g/L ........ 0.03 g/L ...... 0.05 g/L ...... 0.3 g/L ........ 0.2 g/L ........ 0.04 g/L ...... 0.07 g/L ...... | EPTDS .............. EPTDS .............. EPTDS .............. EPTDS .............. EPTDS .............. EPTDS .............. EPTDS .............. EPTDS .............. EPTDS .............. | 1/1/2018–12/31/2020. 1/1/2018–12/31/2020. 1/1/2018–12/31/2020. 1/1/2018–12/31/2020. 1/1/2018–12/31/2020. 1/1/2018–12/31/2020. 1/1/2018–12/31/2020. 1/1/2018–12/31/2020. 1/1/2018–12/31/2020. |
| --- | --- | --- | --- | --- | --- |

Brominated Haloacetic Acid (HAA) Groups de

| HAA5 .......................... HAA6Br ....................... HAA9 .......................... | N/A ........... N/A ........... N/A ........... | EPA 552.3 or EPA 557. EPA 552.3 or EPA 557. EPA 552.3 or EPA 557. | N/A ............... N/A ............... N/A ............... | D/DBPR HAA lo- cation. D/DBPR HAA lo- cation. D/DBPR HAA lo- cation. | 1/1/2018–12/31/2020. 1/1/2018–12/31/2020. 1/1/2018–12/31/2020. |
| --- | --- | --- | --- | --- | --- |

#### Environmental Protection Agency	§ 141.40

TABLE 1—UCMR CONTAMINANT LIST—Continued

| 1—Contaminant | 2—CAS Registry No. | 3—Analytical methods a | 4—Minimum reporting level b | 5—Sampling location c | 6—Period during which monitoring to be completed |
| --- | --- | --- | --- | --- | --- |

Alcohols

| 1-butanol ..................... 2-methoxyethanol ....... 2-propen-1-ol .............. | 71–36–3 ... 109–86–4 107–18–6 | EPA 541 ................ EPA 541 ................ EPA 541 ................ | 2.0 g/L ........ 0.4 g/L ........ 0.5 g/L ........ | EPTDS .............. EPTDS .............. EPTDS .............. | 1/1/2018–12/31/2020. 1/1/2018–12/31/2020. 1/1/2018–12/31/2020. |
| --- | --- | --- | --- | --- | --- |

Other Semivolatile Chemicals

| butylated hydroxanisole. o-toluidine ................... quinoline ..................... | 25013–16– 5. 95–53–4 ... 91–22–5 ... | EPA 530 ................ EPA 530 ................ EPA 530 ................ | 0.03 g/L ...... 0.007 g/L .... 0.02 g/L ...... | EPTDS .............. EPTDS .............. EPTDS .............. | 1/1/2018–12/31/2020. 1/1/2018–12/31/2020. 1/1/2018–12/31/2020. |
| --- | --- | --- | --- | --- | --- |

List 2: Screening Survey

| Reserved .................... | Reserved | Reserved ............... | Reserved ...... | Reserved ........... | Reserved. |
| --- | --- | --- | --- | --- | --- |

List 3: Pre-Screen Testing

| Reserved .................... | Reserved | Reserved ............... | Reserved ...... | Reserved ........... | Reserved. |
| --- | --- | --- | --- | --- | --- |

Column headings are:

1—Contaminant: The name of the contaminant to be analyzed.

2—CAS (Chemical Abstract Service) Registry Number or Identification Number: A unique number identifying the chemical con- taminants.

3—Analytical Methods: Method numbers identifying the methods that must be used to test the contaminants.

4—Minimum Reporting Level (MRL): The value and unit of measure at or above which the concentration of the contaminant must be measured using the approved analytical methods. If EPA determines, after the first six months of monitoring that the specified MRLs result in excessive resampling, EPA will establish alternate MRLs and will notify affected PWSs and laboratories of the new MRLs. N/A is defined as non-applicable.

5—Sampling Location: The locations within a PWS at which samples must be collected.

6—Period During Which Monitoring to be Completed: The time period during which the sampling and testing will occur for the indicated contaminant.

a The analytical procedures shall be performed in accordance with the documents associated with each method, see para- graph (c) of this section.

b The MRL is the minimum concentration of each analyte that must be reported to EPA.

c With the exception of HAA monitoring, sampling must occur at entry points to the distribution system (EPTDSs), after treat- ment is applied, that represent each non-emergency water source in routine use over the 12-month period of monitoring. Sys- tems that purchase water with multiple connections from the same wholesaler may select one representative connection from that wholesaler. This EPTDS sampling location must be representative of the highest annual volume connections. If the connec- tion selected as the representative EPTDS is not available for sampling, an alternate highest volume representative connection must be sampled. See 40 CFR 141.35(c)(3) for an explanation of the requirements related to the use of representative GW EPTDSs. Sampling for UCMR 4 HAA groups must be conducted at the Disinfectants and Disinfection Byproduct Rule (D/DBPR) sampling locations (40 CFR 141.622).

d UCMR 4 HAA monitoring applies only to those PWSs that are subject to D/DBPR HAA5 monitoring requirements.

e PWSs that purchase 100 percent of their water (‘‘consecutive systems’’) are not required to collect UCMR 4 source water samples for TOC or bromide analyses. Sampling for TOC and bromide must otherwise occur at source water influent locations representing untreated water entering the water treatment plant (i.e., a location prior to any treatment). SW and GWUDI systems subject to the D/DBPR TOC monitoring must use their D/DBPR TOC source water sampling site(s) from 40 CFR 141.132 for UCMR 4 TOC and bromide samples. SW and GWUDI systems that are not subject to D/DBPR TOC monitoring will use their Long Term 2 Enhance Surface Water Treatment Rule (LT2) source water sampling site(s) (40 CFR 141.703) for UCMR 4 TOC and bromide samples. Ground water systems that are subject to the D/DBPRs, and therefore subject to UCMR 4 HAA moni- toring, will take TOC and bromide samples at their influents entering their treatment train. TOC and bromide must be collected at the same time as HAA samples. These indicator samples must be collected at a single source water influent using methods al- ready approved for compliance monitoring. TOC methods include: SM 5310 B, SM 5310 C, SM 5310 D (21st edition), or SM 5310 B–00, SM 5310 C–00, SM 5310 D–00 (SM Online), EPA Method 415.3 (Rev. 1.1 or 1.2). Bromide methods include: EPA Methods 300.0 (Rev. 2.1), 300.1 (Rev. 1.0), 317.0 (Rev. 2.0), 326.0 (Rev. 1.0) or ASTM D 6581–12. The MRLs for the individual HAAs are discussed in paragraph (a)(5)(v) of this section.

  - Sampling requirements—(i) Large systems. If you serve more than 10,000 people and meet the UCMR  applica- bility criteria specified in paragraph (a)(2)(i) of this section, you must com- ply with the requirements specified in paragraphs (a)(4)(i)(A) through (I) of this section. Your samples must be col- lected according to the schedule that you are assigned by EPA or your State, or the schedule that you revised using EPA’s  electronic  data  reporting  system

on or before December 31, 2017. Your schedule must  follow  both  the  timing and  frequency  of  monitoring   specified in Tables 1 and 2 of this section.

- Monitoring period. You must col- lect the samples in one continuous 12- month period for List 1 Assessment Monitoring,  and,  if  applicable,  for  List

- Screening Survey, or List 3 Pre- Screen Testing, during the time frame indicated in column 6 of Table 1, in paragraph (a)(3) of this section. EPA or

#### § 141.40

your State  will  specify  the  month(s) and year(s) in which your monitoring must occur. As specified in § 141.35(c)(5), you  must  contact  EPA  if  you  believe you cannot conduct monitoring accord- ing  to  your  schedule.

- Frequency. You must collect the samples within the timeframe and ac- cording to the frequency specified by contaminant type and water source type  for  each  sampling  location,  as

#### 40 CFR Ch. I (7–1–17 Edition)

specified in Table 2, in this paragraph. For the second or subsequent round of sampling, if a sample location is non- operational for more than one month before and one month after the sched- uled sampling month (i.e., it is not pos- sible for you to sample within the win- dow specified in Table 2, in this para- graph), you must notify EPA as speci- fied in § 141.35(c)(5) to reschedule your sampling.

TABLE 2—MONITORING FREQUENCY BY CONTAMINANT AND WATER SOURCE TYPES

| Contaminant type | Water source type | Timeframe | Frequency 1 |
| --- | --- | --- | --- |
| List 1 Cyanotoxins Chemicals. List 1 Contami- nants—Addi- tional Chemi- cals. | Surface water or Ground water under the direct influ- ence of surface water (GWUDI). Surface water or GWUDI ....... Ground water ......................... | March–Novem- ber. 12 months ...... 12 months ...... | You must monitor twice a month for four consecutive months (total of eight sampling events). Sample events must occur two weeks apart. You must monitor for four consecutive quarters. Sample events must occur three months apart. (Example: If first monitoring is in January, the second monitoring must occur any time in April, the third any time in July and the fourth any time in October). You must monitor twice in a consecutive 12-month period. Sample events must occur 5–7 months apart. (Example: If the first monitoring event is in April, the second moni- toring event must occur any time in September, October or November). |

1 Systems must assign a sample event code for each contaminant listed in Table 1. Sample event codes must be assigned by the PWS for each sample event. For more information on sample event codes see § 141.35(e) Table 1.

- Location. You must collect sam- ples for each List 1 Assessment Moni- toring contaminant, and, if applicable, for each List 2 Screening Survey, or List 3 Pre-Screen Testing  contaminant, as specified in Table 1, in paragraph (a)(3) of this section. Samples must be collected at each sample point that is specified in column 5 and footnote c of Table 1, in paragraph (a)(3) of this sec- tion. PWSs conducting List 1 moni- toring for the brominated HAA groups must collect TOC and bromide samples as specified in footnote d of Table 1, in paragraph (a)(3) of this section. If you are a GW system with multiple EPTDSs, and you request and receive approval from EPA or the State for sampling  at  representative  EPTDS(s), as specified in § 141.35(c)(3), you must collect your samples from the approved representative sampling location(s).

- Sampling instructions. For each List 1 Assessment Monitoring contami- nant, and, if applicable, for each List 2 Screening Survey, or List 3 Pre-Screen Testing contaminant, you must follow the sampling procedure for the method specified  in  column  3  of  Table  1,  in

paragraph (a)(3) of this section. In addi- tion, you must not composite (that is, combine, mix, or blend) the samples; you must collect and preserve each sample separately.

- Sample collection and shipping time. If you must ship the samples for anal- ysis, you must collect the  samples early enough in the day to allow ade- quate time to send the samples for overnight delivery to the laboratory. You should not collect samples on Fri- day, Saturday, or Sunday because sam- pling on these days may not allow sam- ples to be shipped and received at the laboratory at the required tempera- ture, unless you have made special ar- rangements with your laboratory to re- ceive the samples.

- Analytical methods. For each con- taminant, you must use the respective analytical methods for List 1, and, if applicable, for List 2, or List 3 that are specified in column 3 of Table 1, in paragraph (a)(3) of this section; report values at or above the minimum re- porting levels for List 1, and, if applica- ble,  for  List  2  Screening  Survey,  or List   3   Pre-Screen   Testing,   that   are

#### Environmental Protection Agency	§ 141.40

specified in column 4 of Table 1, in paragraph (a)(3) of this section; and conduct the quality control procedures specified in paragraph (a)(5) of this sec- tion.

- Laboratory errors or sampling devi- ations. If the laboratory data do not meet the required QC criteria, as speci- fied in paragraph (a)(5) of this section, or you do not follow the required sam- pling procedures, as specified in para- graphs (a)(4) of this section, you must resample within 30 days of being in- formed or becoming aware of  these facts. This resampling is not for the purpose of confirming previous results, but to correct the sampling or labora- tory error. All systems must report the results obtained from the first  sam- pling for each sampling period, except for cases of sampling or laboratory er- rors. For the purposes of this rule, no samples are to be recollected for the purposes of confirming the results ob- served in a previous sampling.

- Analysis. For the List 1 contami- nants, and, if applicable, List 2  Screen- ing Survey, or List 3 Pre-Screen  Test- ing contaminants, identified in Table 1, paragraph (a)(3) of this section,  you must arrange for testing by a labora- tory that has been approved by EPA according to requirements  in  para- graph (a)(5)(ii) of this section.

- Review and reporting of results. After you have received the laboratory results, you must review, approve, and submit the system information, and sample collection data and test results. You must report the results as pro- vided in § 141.35(c)(6).

- Small systems. If you serve 10,000 or fewer people and are notified that you are part of the State Monitoring Plan for Assessment Monitoring, Screening Survey or Pre-Screen moni- toring, you must comply with the re- quirements specified in paragraphs (a)(4)(ii)(A) through (H) of this section. If EPA or the State informs you that they will be collecting your UCMR samples, you must assist them in iden- tifying the appropriate sampling loca- tions and in collecting the samples.

  - Monitoring period and frequency. You must collect samples at the times specified for you by the State or EPA. Your schedule must follow both the timing of monitoring specified in Table

1, List 1, and, if applicable, List  2,  or List 3, and the frequency of monitoring in Table 2 of this section.

  - Location. You must collect sam- ples at the locations specified for you by the State or EPA.

  - Sample kits. You must store and maintain the sample collection  kits sent to you by the UCMR Sampling Co- ordinator in accordance with the kit’s instructions. The sample kit will in- clude all necessary containers, packing materials and cold packs, instructions for collecting the sample and sample treatment (such as dechlorination or preservation), report forms for each sample, contact name and telephone number for the laboratory, and a pre- paid return shipping docket and return address label. If any of the materials listed in the kit’s instructions are not included in the kit or arrive damaged, you must notify the UCMR Sampling Coordinator who sent you the sample collection  kits.

  - Sampling instructions. You must comply with the instructions sent to you by the State or EPA  concerning the use of containers, collection (how to fill the sample  bottle), dechlorination and/or preservation, and sealing and preparation of sample and shipping containers for shipment. You must not composite (that is, combine, mix, or blend) the samples. You also must collect, preserve, and test each sample separately. You must also com- ply with the instructions sent  to  you by the UCMR Sampling Coordinator concerning the handling of sample con- tainers for specific contaminants.

  - Sampling deviations. If you do not collect a sample according to the in- structions provided to you for a listed contaminant, you must report the de- viation within 7 days of the scheduled monitoring on the sample reporting form, as specified in § 141.35(d)(2). You must resample following instructions that you will be sent from the UCMR Sampling Coordinator or State.  A  copy of the form must be sent to the labora- tory with the recollected  samples,  and to the UCMR Sampling Coordinator.

  - [Reserved]

  - Sampling forms. You must com- pletely fill out each of the sampling forms and bottles sent to you by the

#### § 141.40

UCMR Sampling Coordinator,  includ- ing data elements listed in § 141.35(e) for    each    sample,    as    specified    in

§ 141.35(d)(2).  You  must  sign  and  date the   sampling   forms.

  - Sample collection and shipping. You must collect the samples early enough in the day to allow adequate time to send the samples for overnight delivery to the laboratory. You should not collect samples on Friday, Satur- day, or Sunday because sampling on these days may not allow samples to be shipped and received at the laboratory at the required temperature unless you have made special arrangements with EPA for the laboratory to receive the samples. Once you have collected the samples and completely filled in the sampling forms, you must send the samples and the sampling forms to the laboratory designated on the air bill.

- Phased sample analysis for microcystins. You must collect the three required samples (one each for EPA Methods 544, 545 and 546 (ELISA) at the EPTDS) for each sampling event, but not all samples may need to be ana- lyzed. If the  Method  546  ELISA  result is less than 0.3 g/L, report that result and do not analyze the EPA Method 544 sample for that sample event. If the Method 546 ELISA result  is  greater than or equal to 0.3 g/L, report the value and analyze  the  other microcystin  sample  using  EPA  Method

544. You must analyze the EPA Method

545 sample for each sample event for Cylindrospermopsin and anatoxin-a only.

  - Quality control  requirements.  If your system serves more than 10,000 people, you must ensure that  the  qual- ity control  requirements  listed  below are met during your sampling proce- dures and by the laboratory conducting your analyses. You  must  also  ensure that all method quality control proce- dures and all UCMR quality control procedures  are  followed.

- Sample collection/preservation. You must follow the sample collection and preservation requirements for the spec- ified method for each of the contami- nants in Table 1, in paragraph (a)(3) of this section. These requirements speci- fy sample containers, collection, dechlorination, preservation, storage, sample  holding  time,  and  extract  stor-

#### 40 CFR Ch. I (7–1–17 Edition)

age and/or holding time that you must assure that the laboratory follow.

- Laboratory approval for Lists 1, List 2 and List 3. To be approved to conduct UCMR testing, the laboratory must be certified under § 141.28 for one or more compliance analyses; demonstrate for each analytical method it plans to  use for UCMR testing that it can meet the Initial Demonstration of Capability (IDC) requirements detailed in the ana- lytical methods specified in  column  3 of Table 1, in paragraph (a)(3) of this section; and successfully participate in the UCMR Proficiency Testing (PT) Program administered by EPA for each analytical method it plans to use for UCMR testing. UCMR laboratory ap- proval decisions will be granted on an individual method basis for the meth- ods listed in column 3 of Table 1 in paragraph (a)(3) of this section for List 1, List 2, and List 3 contaminants. Lab- oratory approval  is  contingent  upon the capability of the laboratory to post monitoring data to the EPA electronic data reporting system. To  participate in the UCMR Laboratory Approval Pro- gram, the laboratory  must  complete and submit the necessary registration forms by February 21, 2017, and nec- essary application material April 19, 2017. Correspondence must be addressed to: UCMR Laboratory Approval Coordi- nator, USEPA, Technical Support Cen- ter, 26 West Martin Luther King Drive, (MS 140), Cincinnati, OH 45268; or emailed	to	EPA	at: UCMRlSamplinglCoordinator@epa.gov.

- Minimum Reporting Level. The MRL is an estimate of the quantitation limit. Assuming good instrumentation and experienced analysts, an MRL is achievable, with 95% confidence, by 75% of laboratories nationwide.

- Validation of laboratory perform- ance. Your laboratory must be capable of quantifying each contaminant  listed in Table 1, at or below the MRL speci- fied in column 4 of Table 1, in para- graph (a)(3) of this section. You must ensure that the laboratory completes and has on file and available for your inspection, records of two distinct pro- cedures. First, your laboratory must have conducted an IDC involving rep- licate analyses at or below the MRL as described in this paragraph. Second, for

#### Environmental Protection Agency	§ 141.40

each day that  UCMR analyses are con- ducted by your laboratory, a validation of its ability to quantify each contami- nant, at or below the MRL specified in column 4 of Table 1, in paragraph (a)(3) of this section, following the procedure listed in paragraph (a)(5)(iii)(B) of this section, must be performed. The proce- dure for initial validation of laboratory performance at or below the MRL is as follows:

  - All laboratories performing anal- ysis under UCMR must demonstrate that they are capable of meeting data quality objectives at or below the MRL listed in Table 1, column 4, in para- graph (a)(3) of this section.

  - The MRL, or any concentration below the MRL, at which performance is being evaluated, must be contained within the range of calibration. The calibration curve regression model and the range of calibration levels that are

used in these performance validation steps must be used in all routine sam- ple analyses used to comply with this regulation. Only straight line or quad- ratic regression models are  allowed. The use of either weighted or unweighted models is permitted. The use of cubic regression models is not permitted.

  - Replicate analyses of at least seven (7) fortified samples in reagent water must be performed at or below the MRL for each analyte, and must be processed through the entire method procedure (i.e., including extraction, where applicable, and with all preserv- atives).

  - A prediction interval of results (PIR), which is based on the estimated arithmetic mean of  analytical  results and the estimated sample standard de- viation of measurement results, must be determined by Equation 1:

Equation 1	PIR = Mean st

(df , 1/ 2) 

## 11

n

Where:

t is the Student’s t value with df degrees of freedom and confidence level (1–a),

s is the sample standard deviation of n rep-

## C = t

(df , 1/ 2) 

## 11

n

licate samples fortified at the MRL,

n is the number of replicates.

  - The values needed to calculate the PIR using Equation 1 are: Number of replicates (n); Student’s t value with a two-sided 99% confidence level for n number of replicates; the average (mean) of at least seven replicates; and the sample  standard  deviation.  Factor 1 is referred to as the  Half Range PIR (HRPIR).

is constant, and can be tabulated ac- cording to replicate number and con- fidence level for the Student’s t. Table

- in this paragraph lists the constant factor (C) for replicate sample numbers 7 through 10 with a confidence level of 99% for Student’s t.

  - The HRPIR is calculated by Equa- tion 2:

## Equation 2

1

HR PIR   =  sC

HR PIR   =  st

(df , 1/ 2) 1

## n

  - The PIR is calculated by Equation

3:

For a certain number of replicates and for a certain confidence level in Stu- dent’s t, this factor

## Equation 3	PIR = Mean HR

PIR

#### § 141.40

40 CFR Ch. I (7–1–17 Edition)

TABLE 3—THE CONSTANT FACTOR (C) TO BE MULTIPLIED BY THE STANDARD DEVIATION TO

DETERMINE THE HALF RANGE INTERVAL OF THE PIR (STUDENT’S t 99% CONFIDENCE LEVEL) A

| Replicates | Degrees of freedom | Constant factor (C) to be multiplied by the standard deviation |
| --- | --- | --- |
| 7 | 6 | 3.963 |
| 8 | 7 | 3.711 |
| 9 | 8 | 3.536 |
| 10 | 9 | 3.409 |

a The critical t-value for a two-sided 99% confidence interval is equivalent to the critical t-value for a one-sided 99.5% con- fidence interval, due to the symmetry of the t-distribution. PIR = Prediction Interval of Results.

  - The lower and upper result limits of the PIR must be converted to per- cent recovery of  the  concentration being tested. To pass criteria at a cer- tain level, the PIR lower  recovery  lim- its cannot be lower than the lower re- covery limits of the QC interval (50%), and the PIR upper recovery limits can- not be greater than the upper recovery limits of the QC interval (150%). When either of the PIR recovery limits falls outside of either bound of the QC inter- val of recovery (higher than 150% or less than 50%), laboratory performance is not validated at the concentration evaluated. If the PIR limits are con- tained within both bounds of the QC in- terval, laboratory performance is vali- dated for that analyte.

- Quality control requirements for validation of laboratory performance at or below the MRL.

- You must ensure that the calibra- tion curve regression model and that the range of calibration levels that are used in these performance validation steps are used in future routine sample analysis. Only straight line  or  quad- ratic regression models are  allowed. The use of either weighted or unweighted models is permitted. The use of cubic regression models is not permitted.

- You must ensure, once your lab- oratory has performed an IDC as speci- fied in each analytical method (dem- onstrating that DQOs are met at or below an MRL), that a daily perform- ance check is performed for each analyte and method. A single labora- tory blank, fortified at or below the MRL for each analyte, must be proc- essed through the entire method proce- dure. The measured concentration for

each analyte must be converted to a percent recovery, and if the recovery is within 50%–150% (inclusive), the daily performance of the laboratory has been validated. The results for any analyte for which 50%–150% recovery cannot be demonstrated during the daily  check are not valid. Laboratories  may  elect to re-run the daily performance check sample if the performance for any analyte or analytes cannot be vali- dated. If performance is validated for these analytes, the laboratory perform- ance is considered validated. Alter- natively, the laboratory may re-cali- brate and repeat the performance vali- dation process for all analytes.

- Laboratory fortified sample matrix and laboratory fortified sample matrix du- plicate. You must ensure that your lab- oratory prepares and analyzes the Lab- oratory Fortified  Sample  Matrix (LFSM) sample for accuracy and Lab- oratory Fortified Sample Matrix Dupli- cate (LFSMD) samples for precision to determine method accuracy and preci- sion for all contaminants in Table 1, in paragraph (a)(3) of this section. LFSM/ LFSMD samples must  be  prepared using a sample collected  and  analyzed in accordance with UCMR  require- ments and analyzed at a frequency  of 5% (or 1 LFSM/LFSMD set per every 20 samples) or with each sample batch, whichever is more frequent. In addi- tion, the LFSM/LFSMD fortification concentrations must be alternated be- tween a low-level fortification and mid-level fortification approximately 50% of the time. (For example: A set of 40 samples will require preparation and analysis of 2 LFSM/LFSMD paired samples.  The  first  LFSM/LFSMD paired  sample  set  must  be  fortified  at

#### Environmental Protection Agency	§ 141.40

either the low-level or mid-level, and the second LFSM/LFSMD paired sam- ple set must be fortified with the other standard, either the low-level or mid- level, whichever was not used for the initial LFSM/LFSMD paired  sample set.) The low-level LFSM/LFSMD for- tification concentration must be  with- in 50% of the MRL for each contami- nant (e.g., for an MRL of 1 g/L the ac- ceptable fortification levels must be between 0.5 g/L and 1.5 g/L). The mid- level LFSM/LFSMD fortification con- centration must be within 20% of the mid-level calibration standard for each contaminant, and is to represent, where possible and where the labora- tory has data from previously analyzed samples,  an  approximate  average  con-

centration observed in previous anal- yses of that analyte. There are  no UCMR contaminant recovery accept- ance criteria specified for LFSM/ LFSMD analyses. All  LFSM/LFSMD data are to be reported.

- Method defined quality control. You must ensure that your laboratory ana- lyzes Laboratory Fortified Blanks and conducts Laboratory Performance Checks, as appropriate to the method’s requirements, for those methods listed in Table 1, column 3, in  paragraph (a)(3) of this section. Each method specifies acceptance criteria for these QC checks. The following HAA results must be reported using EPA’s elec- tronic data reporting system for  qual- ity control purposes.

470

§ 141.40

TABLE 4—HAA QC RESULTS

| 1—Contaminant | 2—CAS Registry No. | 3—Analytical methods a | 4—Minimum reporting level b | 5—HAA6Br Group | 6—HAA9 Group | 7—HAA5 Group |
| --- | --- | --- | --- | --- | --- | --- |

##### Brominated Haloacetic Acid (HAA) Groups

| Bromochloroacetic acid (BCAA) Bromodichloroacetic acid (BDCAA). Chlorodibromoacetic acid (CDBAA). Tribromoacetic acid (TBAA) ....... Monobromoacetic acid (MBAA) Dibromoacetic acid (DBAA) ....... Dichloroacetic acid (DCAA) ........ Monochloroacetic acid (MCAA) .. Trichloroacetic acid (TCAA) ....... | 5589–96–8 71133–14–7 5278–95–5 75–96–7 79–08–3 631–64–1 79–43–6 79–11–8 76–03–9 | EPA 552.3 or EPA 557 ...... EPA 552.3 or EPA 557 ...... EPA 552.3 or EPA 557 ...... EPA 552.3 or EPA 557 ...... EPA 552.3 or EPA 557 ...... EPA 552.3 or EPA 557 ...... EPA 552.3 or EPA 557 ...... EPA 552.3 or EPA 557 ...... EPA 552.3 or EPA 557 ...... | 0.3 g/L. 0.5 g/L. 0.3 g/L ........ 2.0 g/L. 0.3 g/L. 0.3 g/L ........ 0.2 g/L. 2.0 g/L ........ 0.5 g/L. | HAA6Br | HAA9 |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | HAA5 |

Column headings are:

1—Contaminant: The name of the contaminant to be analyzed.

2—CAS (Chemical Abstract Service) Registry Number or Identification Number: A unique number identifying the chemical contaminants.

3—Analytical Methods: Method numbers identifying the methods that must be used to test the contaminants.

40 CFR Ch. I (7–1–17 Edition)

4—Minimum Reporting Level (MRL): The value and unit of measure at or above which the concentration of the contaminant must be meas- ured using the approved analytical methods. If EPA determines, after the first six months of monitoring that the specified MRLs result in ex- cessive resampling, EPA will establish alternate MRLs and will notify affected PWSs and laboratories of the new MRLs.

5–7—HAA groups identified in paragraph (a)(3) of this section to be monitored as UCMR contaminants.

a The analytical procedures shall be performed in accordance with the documents associated with each method, see paragraph (c) of this section, and must meet all quality control requirements outlined paragraph (a)(5) of this section.

b The MRL is the minimum concentration of each analyte that must be reported to EPA.

#### Environmental Protection Agency	§ 141.40

- Reporting. You must require your laboratory to submit these data elec- tronically to the State and EPA using EPA’s electronic data reporting sys- tem, accessible, within 120 days from the sam- ple collection date. You then have 60 days from when the laboratory posts the data to review, approve and submit the data to the  State  and  EPA,  via EPA’s electronic data reporting sys- tem. If you do not electronically ap- prove and submit the  laboratory  data to EPA within 60 days of the labora- tory posting data to EPA’s electronic reporting system, the data will be con- sidered approved and available for State and EPA review.

(6) Violation of this rule—(i) Monitoring violations. Any failure to monitor in ac- cordance with § 141.40(a)(3)–(5) is a mon- itoring   violation.

(ii)  Reporting  violations.  Any   failure to report  in  accordance  with  § 141.35  is a   reporting   violation.

- Petitions and waivers by States—(1) Governors’ petition for additional con- taminants. The Safe  Drinking  Water Act allows Governors of seven (7) or more States to petition the EPA Ad- ministrator to add one or more con- taminants to the UCMR Contaminant List in paragraph (a)(3) of this section. The petition must clearly identify the reason(s) for adding the contaminant(s) to the monitoring list, including the potential risk to public health, particu- larly any information that might be available regarding disproportional risks to the health and safety of chil- dren, the expected occurrence docu- mented by any available data, any ana- lytical methods known or proposed to be used to test for the contaminant(s), and any other information that could assist the Administrator in deter- mining which contaminants present the greatest public health concern and should, therefore, be included on the UCMR Contaminant List in paragraph (a)(3) of this section.

(2) State-wide waivers. A State can waive monitoring requirements only with EPA approval and under very lim- ited conditions. Conditions and proce- dures for obtaining a waiver are as fol- lows:

- Application. A State may apply to EPA for a State-wide waiver from the

unregulated contaminant monitoring requirements for PWSs serving more than 10,000 people. To apply for such a waiver, the State must submit an ap- plication to EPA that includes the fol- lowing information: The list of con- taminants on the UCMR Contaminant List for which a waiver is requested, along with documentation for each contaminant in the request dem- onstrating that the contaminants or their parent compounds do not occur naturally in the State, and certifying that during the past 15 years they have not been used, applied, stored, disposed of, released, or detected in the source waters or distribution systems in the State.

- Approval. EPA will review State applications and notify the State whether it accepts or rejects the re- quest. The State must receive written approval from EPA before issuing a State-wide waiver.

- Incorporation  by  reference.  These standards    are    incorporated    by    ref- erence  into  this  section  with  the  ap- proval  of  the  Director  of  the  Federal Register  under  5  U.S.C.  552(a)  and  1 CFR  part  51.  All  approved  material  is available   for   inspection   either   elec- tronically   in   hard   copy   at   the   Water   Docket, EPA/DC,  and  from  the  sources  as  fol- lows.  The  Public  Reading  Room  (EPA West,  Room  3334,  1301  Constitution Ave.   NW.,   Washington,   DC)   is   open from  8:30  a.m.  to  4:30  p.m.,  Monday through   Friday,   excluding   legal   holi- days.  The  telephone  number  for  this Public Reading Room is (202) 566–1744, and   the   telephone   number   for   the Water Docket is (202) 566–2426. The ma- terial is also available for inspection at the National Archives and Records Ad- ministration   (NARA).   For   information on  the  availability  of  this  material  at NARA, call (202) 741–6030

  - U.S. Environmental Protection Agency, Water Docket, EPA/DC, EPA West, Room 3334, 1301 Constitution Ave. NW., Washington, DC 20004.

- Method 200.8 ‘‘Determination of Trace Elements in Waters and  Wastes by Inductively Coupled Plasma—Mass Spectrometry,’’    Revision    5.4,    EMMC

#### § 141.40

Version, 1994. Available on the Internet

- Method 300.0 ‘‘Determination of Inorganic Anions by Ion Chroma- tography Samples,’’ Revision 2.1, Au- gust 1993. Available on the Internet at v.

- Method 300.1 ‘‘Determination of Inorganic Anions in Drinking Water by Ion    Chromatography,’’    Revision    1.0, 1997.   Available   on   the   Internet   at

- Method 317.0 ‘‘Determination of Inorganic Oxyhalide Disinfection By- Products in Drinking Water Using Ion Chromatography with the Addition of a Postcolumn Reagent for Trace Bro- mate Analysis,’’ Revision 2.0, July 2001, EPA 815–B–01–001. Available on the Internet	.

- Method 326.0 ‘‘Determination of Inorganic Oxyhalide Disinfection By- Products in Drinking Water Using Ion Chromatography Incorporating the Ad- dition of a Suppressor Acidified Postcolumn Reagent for Trace Bro- mate Analysis,’’ Revision  1.0,  June 2002, EPA 815–R–03–007. Available on the Internet.

- Method  415.3  ‘‘Determination  of Total  Organic  Carbon  and  Specific  UV Absorbance at 254 nm in Source Water and    Drinking    Water,’’    Revision    1.1, February 2005, EPA/600/R–05/055. Avail- able	on	the	Internet

- Method 415.3 ‘‘Determination of Total  Organic  Carbon  and  Specific  UV Absorbance at 254 nm in Source Water and    Drinking    Water,’’    Revision    1.2, September	2009,	EPA/600/R–09/122. Available   on   the

- Method 525.3 ‘‘Determination of Semivolatile     Organic     Chemicals     in Drinking  Water  by  Solid  Phase  Extrac- tion  and  Capillary  Column  Gas  Chro- matography/Mass   Spectrometry   (GC/ MS),’’ Version 1.0, February 2012, EPA/ 600/R–12/010. Available on the Internet.

- Method  530  ‘‘Determination  of Select   Semivolatile   Organic   Chemicals

#### 40 CFR Ch. I (7–1–17 Edition)

in Drinking Water by Solid Phase Ex- traction  and  Gas  Chromatography/ Mass Spectrometry (GC/MS),’’ Version 1.0,  January  2015,  EPA/600/R–14/442.

Available   on   the   Internet   .

- EPA Method 541: ‘‘Determination of	1-Butanol,	1,4-Dioxane,	2- Methoxyethanol and 2-Propen-1-ol in Drinking Water by Solid Phase Extrac- tion and Gas Chromatography/Mass Spectrometry,’’ November 2015, EPA 815–R–15–011. Available on the Internet.

- Method  544  ‘‘Determination  of Microcystins  and  Nodularin  in  Drink- ing   Water   by   Solid   Phase   Extraction and    Liquid    Chromatography/Tandem Mass	Spectrometry	(LC/MS/MS),’’ Version 1.0, February 2015, EPA 600–R– 14/474.  Available  on  the  .

- EPA   Method   545:   ‘‘Determina- tion	of	Cylindrospermopsin	and Anatoxin-a   in   Drinking   Water   by   Liq- uid   Chromatography   Electrospray   Ion- ization     Tandem     Mass     Spectrometry (LC/ESI–MS/MS),’’ April 2015, EPA 815– R–15–009.  Available  on  the  .

- EPA  Method  546:  ‘‘Determina- tion	of	Total	Microcystins	and Nodularins in Drinking Water and Am- bient  Water  by  Adda  Enzyme-Linked Immunosorbent  Assay,’’  August  2016, EPA–815–B–16–011.   Available   on   the Internet		.

- Method 552.3 ‘‘Determination of Haloacetic Acids and Dalapon in Drinking Water by Liquid-Liquid Microextraction,  Derivatization,  and Gas Chromatography with Electron Capture Detection,’’ Revision 1.0, July 2003, EPA 815–B–03–002. Available on the Internet.

- EPA  Method  557:  ‘‘Determina- tion  of  Haloacetic  Acids,  Bromate,  and Dalapon   in   Drinking   Water   by   Ion Chromatography    Electrospray    Ioniza- tion  Tandem  Mass  Spectrometry  (IC– ESI–MS/MS),’’  Version  1.0,  September 2009, EPA  815–B–09–012.  Available  on

#### Environmental Protection Agency	§ 141.41

the    Internet    .

  - American Public Health Associa- tion—Standard Test Method for Ele- ments in Water by Inductively Coupled Plasma-Mass Spectrometry,’’ approved August 1, 2010. Available for purchase on the Internet.

- ‘‘Standard Methods for the Exam- ination of Water & Wastewater,’’ 21st edition (2005).

- SM 3125 ‘‘Metals by Inductively Coupled  Plasma/Mass  Spectrometry.’’

- SM 5310B ‘‘Total Organic Carbon (TOC): High-Temperature Combustion Method.’’

- SM 5310C ‘‘Total Organic Carbon (TOC): Persulfate-UV or Heated- Persulfate  Oxidation  Method.’’

- SM 5310D ‘‘Total Organic Carbon (TOC): Wet-Oxidation Method.’’

- The following methods are from ‘‘Standard Methods Online.,’’ approved 2000 (unless noted). Available for pur- chase on the Internet

  - SM 3125 ‘‘Metals by Inductively Coupled Plasma/Mass Spectrometry’’ Editorial revisions, 2011 (SM 3125–09).

  - SM 5310B ‘‘Total Organic Carbon: High-Temperature Combustion  Meth- od,’’ (5310B–00).

  - SM 5310C ‘‘Total Organic Carbon: Persulfate-UV or Heated-Persulfate Oxidation Method,’’ (5310C–00).

  - SM 5310D ‘‘Total Organic Carbon: Wet-Oxidation Method,’’ (5310D–00).

  - ASTM International, 100 Barr Harbor Drive, West Conshohocken, PA 19428–2959.

- ASTM D5673–10 ‘‘Standard Test Method for Elements in Water by In- ductively Coupled Plasma-Mass Spec- trometry,’’ approved August 1, 2010. Available for purchase on  the  Internet at	.

- ASTM D6581–12 ‘‘Standard Test Methods for Bromate, Bromide, Chlo- rate, and Chlorite in Drinking  Water by Suppressed Ion Chromatography,’’ approved March 1, 2012. Available for purchase on the Internet

[72  FR 393,  Jan. 4,  2007;  72  FR 3916,  Jan. 26,

2007, as amended at 77 FR 26098, May 2, 2012;

81 FR 92688, Dec. 20, 2016]

##### § 141.41   Special    monitoring    for    so- dium.

- Suppliers of water for community public water systems shall collect and analyze one sample per plant at the entry point of the distribution system for the determination of sodium con- centration levels; samples must be col- lected and analyzed annually for sys- tems utilizing surface water sources in whole or in part, and at least every three years for systems utilizing solely ground water sources. The minimum number of samples required to be taken by the system shall be based on the number of treatment plants used by the system, except that multiple wells drawing raw water from a single aqui- fer may, with the State approval, be considered one treatment plant for de- termining the minimum number of samples. The supplier of water may be required by the State to collect and analyze water samples for sodium more frequently in locations  where the so- dium content is variable.

- The supplier of water shall report to EPA and/or the State the  results  of the analyses for  sodium  within  the first 10 days of the month following the month in which the sample  results were received or within the first 10 days following the end of the required monitoring period as stipulated by the State, whichever of these  is  first.  If more than annual sampling is required the supplier shall report the average sodium concentration within 10 days of the month following the month in which the analytical results of the last sample used for the annual average was received. The supplier of water shall not be required to report the results to EPA where the State has adopted this regulation and results are reported to the State. The supplier shall report the results to EPA where the State has not adopted this regulation.

- The supplier of water shall notify appropriate local and State  public health officials of the sodium levels by written notice by direct mail  within three months. A copy of each notice re- quired to be provided by this paragraph shall be sent to EPA and/or the State within 10 days of its issuance. The sup- plier of water is not required to notify appropriate local and State  public health   officials   of   the   sodium   levels

#### § 141.42

where  the  State  provides  such  notices in lieu of the supplier.

- Analyses for sodium shall be con- ducted as directed in § 141.23(k)(1).

[45 FR 57345, Aug. 27, 1980, as amended at 59

FR 62470, Dec. 5, 1994]

##### § 141.42   Special	monitoring	for corrosivity characteristics.

(a)–(c) [Reserved]

(d) Community water supply systems shall identify whether the following construction materials are present in their distribution system and report to the State:

Lead from piping, solder, caulking, interior lining of distribution mains, alloys and home plumbing.

Copper from piping and alloys, service lines, and home plumbing.

Galvanized  piping,  service  lines,  and  home plumbing.

Ferrous piping materials  such as cast  iron and steel.

Asbestos cement pipe.

In addition, States may require identi- fication and reporting of other mate- rials of construction present in dis- tribution systems that may contribute contaminants to the drinking water, such as:

Vinyl lined asbestos cement pipe. Coal tar lined pipes and tanks.

[45 FR 57346, Aug. 27, 1980; 47 FR 10999, Mar.

12, 1982, as amended at 59 FR 62470, Dec. 5,

1994]

##### § 141.43   Prohibition   on   use   of   lead pipes, solder, and flux.

- In general—(1) Prohibition. Any pipe, solder, or flux, which is used after June 19, 1986, in the installation or re- pair of—

- Any public water system, or

- Any plumbing in a residential or nonresidential facility providing water for human consumption which is con- nected to a public water  system  shall be lead free as defined by paragraph (d) of this section. This paragraph (a)(1) shall not apply to leaded joints nec- essary for the repair of cast iron pipes.

(2)  [Reserved]

- State enforcement—(1) Enforcement of prohibition. The requirements of paragraph (a)(1) of this section shall be enforced in all States effective June 19, 1988. States shall enforce such require- ments through State or local plumbing

#### 40 CFR Ch. I (7–1–17 Edition)

codes, or such other means of enforce- ment as the State may determine to be appropriate.

(2)  [Reserved]

- Penalties. If the Administrator de- termines that a State is not  enforcing the requirements of paragraph (a) of this section, as required pursuant to paragraph (b) of this section, the Ad- ministrator may withhold up to 5 per- cent of Federal funds available to that State for State program grants under section 1443(a) of the Act.

- Definition of lead free. For pur- poses of this section, the term lead free:

- When used with respect to solders and flux refers to solders and flux con- taining not more than 0.2 percent lead;

- When used with respect to pipes and pipe fittings refers to pipes and pipe  fittings  containing  not  more  than

8.0 percent lead; and

- When used with respect to plumb- ing fittings and fixtures intended by the manufacturer to dispense water for human ingestion refers to fittings and fixtures that are in compliance with standards established in accordance with 42 U.S.C. 300g–6(e).

[52 FR 20674, June 2, 1987, as amended at 65

FR 2003, Jan. 12, 2000]

# Subpart F—Maximum Contami- nant Level Goals and Max- imum Residual Disinfectant Level Goals

##### § 141.50   Maximum   contaminant   level goals for organic contaminants.

  - MCLGs are zero for the following contaminants:

    - Benzene

    - Vinyl chloride

    - Carbon  tetrachloride

    - 1,2-dichloroethane

    - Trichloroethylene

    - Acrylamide

    - Alachlor

    - Chlordane

    - Dibromochloropropane

    - 1,2-Dichloropropane

    - Epichlorohydrin

    - Ethylene dibromide

    - Heptachlor

    - Heptachlor epoxide

    - Pentachlorophenol

Environmental Protection Agency	§ 141.53

    - Polychlorinated	biphenyls (PCBs)

    - Tetrachloroethylene

    - Toxaphene

    - Benzo[a]pyrene

    - Dichloromethane	(methylene chloride)

    - Di(2-ethylhexyl)phthalate

    - Hexachlorobenzene

    - 2,3,7,8-TCDD (Dioxin)

| Contaminant | MCLG in mg/l |
| --- | --- |
| (1) 1,1-Dichloroethylene ........................................ | 0.007 |
| (2) 1,1,1-Trichloroethane ....................................... | 0.20 |
| (3) para-Dichlorobenzene ...................................... | 0.075 |
| (4) Aldicarb ............................................................ | 0.001 |
| (5) Aldicarb sulfoxide ............................................. | 0.001 |
| (6) Aldicarb sulfone ............................................... | 0.001 |
| (7) Atrazine ............................................................ | 0.003 |
| (8) Carbofuran ....................................................... | 0.04 |
| (9) o-Dichlorobenzene ........................................... | 0.6 |
| (10) cis-1,2-Dichloroethylene ................................. | 0.07 |
| (11) trans-1,2-Dichloroethylene ............................. | 0.1 |
| (12) 2,4-D .............................................................. | 0.07 |
| (13) Ethylbenzene ................................................. | 0.7 |
| (14) Lindane .......................................................... | 0.0002 |
| (15) Methoxychlor .................................................. | 0.04 |
| (16) Monochlorobenzene ....................................... | 0.1 |
| (17) Styrene ........................................................... | 0.1 |
| (18) Toluene .......................................................... | 1 |
| (19) 2,4,5-TP ......................................................... | 0.05 |
| (20) Xylenes (total) ................................................ | 10 |
| (21) Dalapon .......................................................... | 0.2 |
| (22) Di(2-ethylhexyl)adipate .................................. | .4 |
| (23) Dinoseb .......................................................... | .007 |
| (24) Diquat ............................................................. | .02 |
| (25) Endothall ........................................................ | .1 |
| (26) Endrin ............................................................. | .002 |
| (27) Glyphosate ..................................................... | .7 |
| (28) Hexachlorocyclopentadiene ........................... | .05 |
| (29) Oxamyl (Vydate) ............................................ | .2 |
| (30) Picloram ......................................................... | .5 |
| (31) Simazine ........................................................ | .004 |
| (32) 1,2,4-Trichlorobenzene .................................. | .07 |
| (33) 1,1,2-Trichloroethane ..................................... | .003 |

MCLGs for the following contami- nants are as indicated:

| Contaminant | MCLG (mg/l) |
| --- | --- |
| Chromium .................................... | 0.1 |
| Copper ......................................... | 1.3 |
| Cyanide (as free Cyanide) .......... | .2 |
| Fluoride ........................................ | 4.0 |
| Lead ............................................. | zero |
| Mercury ........................................ | 0.002 |
| Nitrate .......................................... | 10 (as Nitrogen). |
| Nitrite ........................................... | 1 (as Nitrogen). |
| Total Nitrate + Nitrite ................... | 10 (as Nitrogen). |
| Selenium ...................................... | 0.05 |
| Thallium ....................................... | .0005 |

1 This value for arsenic is effective January 23, 2006. Until then, there is no MCLG.

[50 FR 47155, Nov. 14, 1985, as amended at 52

FR  20674,  June  2,  1987;  56  FR  3593,  Jan.  30,

1991;  56  FR 26548,  June 7,  1991;  56  FR  30280,

July 1, 1991; 57 FR 31846, July 17, 1992; 60 FR

33932, June 29, 1995; 66 FR 7063, Jan. 22, 2001]

##### § 141.52 Maximum contaminant level goals for microbiological contami- nants.

- MCLGs for the following contami- nants are as indicated:

| Contaminant | MCLG |
| --- | --- |
| (1) Giardia lamblia ........................................ | zero |
| (2) Viruses .................................................... | zero |
| (3) Legionella ................................................ | zero |
| (4) Total coliforms (including fecal) .............. | zero |
| coliforms and Escherichia coli. |  |
| (5) Cryptosporidium ...................................... | zero |
| (6) Escherichia coli (E. coli) ......................... | zero |

[50 FR 46901, Nov. 13, 1985, as amended at 52

FR  20674,  June  2,  1987;  52  FR  25716,  July  8,

1987;  56  FR 3592,  Jan. 30,  1991;  56  FR 30280,

July 1, 1991; 57 FR 31846, July 17, 1992]

##### § 141.51   Maximum   contaminant   level goals for inorganic contaminants.

  - [Reserved]

  - MCLGs for the following contami- nants are as indicated:

- The MCLG identified in paragraph (a)(4) of this section is applicable until March 31, 2016. The MCLG identified in paragraph (a)(6) of this section is appli- cable beginning April 1, 2016.

[78 FR 10347, Feb. 13, 2013]

##### § 141.53   Maximum   contaminant   level goals for disinfection byproducts.

| Disinfection byproduct | MCLG (mg/L) |
| --- | --- |
| Bromodichloromethane ............................................ Bromoform ............................................................... Bromate ................................................................... Chlorite .................................................................... Chloroform ............................................................... Dibromochloromethane ........................................... Dichloroacetic acid .................................................. Monochloroacetic acid ............................................. Trichloroacetic acid .................................................. | zero zero zero 0.8 0.07 0.06 zero 0.07 0.02 |

MCLGs for the following disinfection byproducts are as indicated:

Contaminant

MCLG (mg/l)

Antimony ......................................	0.006

Arsenic .........................................	zero 1

Asbestos ......................................	7 Million fibers/liter

(longer than 10 m).

Barium  .........................................	2

Beryllium	004

Cadmium  .....................................	0.005

[63 FR 69465, Dec. 16, 1998, as amended at 65

FR 34405, May 30, 2000; 71 FR 478, Jan. 4, 2006]

#### § 141.54

##### § 141.54   Maximum   residual   disinfect- ant level goals for disinfectants.

MRDLGs for disinfectants are as fol- lows:

| Disinfectant residual | MRDLG(mg/L) |
| --- | --- |
| Chlorine ................................................ Chloramines ......................................... Chlorine dioxide ................................... | 4 (as Cl 2). 4 (as Cl 2). 0.8 (as ClO2) |

[63 FR 69465, Dec. 16, 1998]

##### § 141.55   Maximum   contaminant   level goals for radionuclides.

MCLGs  for  radionuclides  are  as  indi- cated in the following table:

| Contaminant | MCLG |
| --- | --- |
| 1. Combined radium-226 and radium-228 .............. | Zero. |
| 2. Gross alpha particle activity (excluding radon | Zero. |
| and uranium). |  |
| 3. Beta particle and photon radioactivity ................ | Zero. |
| 4. Uranium ............................................................... | Zero. |

[65 FR 76748, Dec. 7, 2000]

# Subpart G—National Primary Drinking Water Regulations: Maximum Contaminant Levels and Maximum Residual Dis- infectant Levels

##### § 141.60   Effective dates.

  - The effective dates for § 141.61 are as  follows:

40 CFR Ch. I (7–1–17 Edition)

- The effective date for paragraphs (a)(1) through (a)(8) of § 141.61 is Janu- ary 9, 1989.

- The effective date for paragraphs (a)(9) through (a)(18) and (c)(1) through (c)(18) of § 141.61 is July 30, 1992.

- The effective date for paragraphs (a)(19) through (a)(21), (c)(19) through (c)(25),  and  (c)(27)  through  (c)(33)  of

§ 141.61 is January 17, 1994. The effective date of § 141.61(c)(26) is August 17, 1992.

  - The effective dates for § 141.62 are as  follows:

    - The effective date of paragraph (b)(1) of § 141.62 is October 2, 1987.

    - The effective date for paragraphs (b)(2)   and   (b)(4)   through   (b)(10)   of

§ 141.62 is July 30, 1992.

    - The effective date for paragraphs (b)(11) through (b)(15) of § 141.62 is Janu- ary 17, 1994.

    - The effective date for § 141.62(b)(16) is January 23, 2006.

[56  FR 3593,  Jan. 30,  1991,  as  amended  at 57

FR 31846,  July 17,  1992;  59  FR 34324,  July 1,

1994; 66 FR 7063, Jan. 22, 2001]

##### § 141.61   Maximum  contaminant  levels for organic contaminants.

      - The following maximum contami- nant levels for organic contaminants apply to community and non-transient, non-community water systems.

| CAS No. | Contaminant | MCL (mg/l) |
| --- | --- | --- |
| (1) 75–01–4 ............................................................ | Vinyl chloride ............................................................. | 0.002 |
| (2) 71–43–2 ............................................................ | Benzene .................................................................... | 0.005 |
| (3) 56–23–5 ............................................................ | Carbon tetrachloride .................................................. | 0.005 |
| (4) 107–06–2 .......................................................... | 1,2-Dichloroethane .................................................... | 0.005 |
| (5) 79–01–6 ............................................................ | Trichloroethylene ....................................................... | 0.005 |
| (6) 106–46–7 .......................................................... | para-Dichlorobenzene ............................................... | 0.075 |
| (7) 75–35–4 ............................................................ | 1,1-Dichloroethylene .................................................. | 0.007 |
| (8) 71–55–6 ............................................................ | 1,1,1-Trichloroethane ................................................ | 0.2 |
| (9) 156–59–2 .......................................................... | cis-1,2-Dichloroethylene ............................................ | 0.07 |
| (10) 78–87–5 .......................................................... | 1,2-Dichloropropane .................................................. | 0.005 |
| (11) 100–41–4 ........................................................ | Ethylbenzene ............................................................. | 0.7 |
| (12) 108–90–7 ........................................................ | Monochlorobenzene .................................................. | 0.1 |
| (13) 95–50–1 .......................................................... | o-Dichlorobenzene .................................................... | 0.6 |
| (14) 100–42–5 ........................................................ | Styrene ...................................................................... | 0.1 |
| (15) 127–18–4 ........................................................ | Tetrachloroethylene ................................................... | 0.005 |
| (16) 108–88–3 ........................................................ | Toluene ...................................................................... | 1 |
| (17) 156–60–5 ........................................................ | trans-1,2-Dichloroethylene ........................................ | 0.1 |
| (18) 1330–20–7 ...................................................... | Xylenes (total) ........................................................... | 10 |
| (19) 75–09–2 .......................................................... | Dichloromethane ....................................................... | 0.005 |
| (20) 120–82–1 ........................................................ | 1,2,4-Trichloro- benzene ........................................... | .07 |
| (21) 79–00–5 .......................................................... | 1,1,2-Trichloro- ethane .............................................. | .005 |

      - The Administrator, pursuant to section 1412 of the Act, hereby identi- fies  as  indicated  in  the  Table  below

granular	activated	carbon	(GAC),

#### Environmental Protection Agency	§ 141.61

packed tower aeration (PTA), or oxida- tion (OX) as the best technology treat- ment technique, or other means avail- able for achieving compliance with the

maximum contaminant level for or- ganic contaminants identified in para- graphs (a) and (c) of this section:

BAT FOR ORGANIC CONTAMINANTS LISTED IN § 141.61 (a) AND (c)

| CAS No. | Contaminant | GAC | PTA | OX |
| --- | --- | --- | --- | --- |
| 15972–60–8 .................................... | Alachlor .............................................................................. | X | X | X |
| 116–06–3 ........................................ | Aldicarb .............................................................................. | X |  |  |
| 1646–88–4 ...................................... | Aldicarb sulfone ................................................................. | X |  |  |
| 1646–87–3 ...................................... | Aldicarb sulfoxide .............................................................. | X |  |  |
| 1912–24–9 ...................................... | Atrazine ............................................................................. | X |  |  |
| 71–43–2 .......................................... | Benzene ............................................................................ | X |  |  |
| 50–32–8 .......................................... | Benzo[a]pyrene ................................................................. | X |  |  |
| 1563–66–2 ...................................... | Carbofuran ......................................................................... | X |  |  |
| 56–23–5 .......................................... | Carbon tetrachloride .......................................................... | X | X |  |
| 57–74–9 .......................................... | Chlordane .......................................................................... | X |  |  |
| 75–99–0 .......................................... | Dalapon ............................................................................. | X |  |  |
| 94–75–7 .......................................... | 2,4-D .................................................................................. | X |  |  |
| 103–23–1 ........................................ | Di (2-ethylhexyl) adipate ................................................... | X | X |  |
| 117–81–7 ........................................ | Di (2-ethylhexyl) phthalate ................................................ | X |  |  |
| 96–12–8 .......................................... | Dibromochloropropane (DBCP) ........................................ | X | X |  |
| 95–50–1 .......................................... | o-Dichlorobenzene ............................................................ | X | X |  |
| 106–46–7 ........................................ | para-Dichlorobenzene ....................................................... | X | X |  |
| 107–06–2 ........................................ | 1,2-Dichloroethane ............................................................ | X | X |  |
| 75–35–4 .......................................... | 1,1-Dichloroethylene .......................................................... | X | X |  |
| 156–59–2 ........................................ | cis-1,2-Dichloroethylene .................................................... | X | X |  |
| 156–60–5 ........................................ | trans-1,2-Dichloroethylene ................................................ | X | X |  |
| 75–09–2 .......................................... | Dichloromethane ............................................................... | .............. | X |  |
| 78–87–5 .......................................... | 1,2-Dichloropropane .......................................................... | X | X |  |
| 88–85–7 .......................................... | Dinoseb ............................................................................. | X |  |  |
| 85–00–7 .......................................... | Diquat ................................................................................ | X |  |  |
| 145–73–3 ........................................ | Endothall ............................................................................ | X |  |  |
| 72–20–8 .......................................... | Endrin ................................................................................ | X |  |  |
| 100–41–4 ........................................ | Ethylbenzene ..................................................................... | X | X |  |
| 106–93–4 ........................................ | Ethylene Dibromide (EDB) ................................................ | X | X |  |
| 1071–83–6 ...................................... | Gylphosate ........................................................................ | .............. | .............. |  |
| 76–44–8 .......................................... | Heptachlor ......................................................................... | X |  |  |
| 1024–57–3 ...................................... | Heptachlor epoxide ........................................................... | X |  |  |
| 118–74–1 ........................................ | Hexachlorobenzene ........................................................... | X |  |  |
| 77–47–3 .......................................... | Hexachlorocyclopentadiene .............................................. | X | X |  |
| 58–89–9 .......................................... | Lindane .............................................................................. | X |  |  |
| 72–43–5 .......................................... | Methoxychlor ..................................................................... | X |  |  |
| 108–90–7 ........................................ | Monochlorobenzene .......................................................... | X | X |  |
| 23135–22–0 .................................... | Oxamyl (Vydate) ................................................................ | X |  |  |
| 87–86–5 .......................................... | Pentachlorophenol ............................................................. | X |  |  |
| 1918–02–1 ...................................... | Picloram ............................................................................. | X |  |  |
| 1336–36–3 ...................................... | Polychlorinated biphenyls (PCB) ....................................... | X |  |  |
| 122–34–9 ........................................ | Simazine ............................................................................ | X |  |  |
| 100–42–5 ........................................ | Styrene .............................................................................. | X | X |  |
| 1746–01–6 ...................................... | 2,3,7,8-TCDD (Dioxin) ....................................................... | X |  |  |
| 127–18–4 ........................................ | Tetrachloroethylene ........................................................... | X | X |  |
| 108–88–3 ........................................ | Toluene .............................................................................. | X | X |  |
| 8001–35–2 ...................................... | Toxaphene ......................................................................... | X |  |  |
| 93–72–1 .......................................... | 2,4,5-TP (Silvex) ................................................................ | X |  |  |
| 120–82–1 ........................................ | 1,2,4-Trichlorobenzene ...................................................... | X | X |  |
| 71–55–6 .......................................... | 1,1,1-Trichloroethane ........................................................ | X | X |  |
| 79–00–5 .......................................... | 1,1,2-Trichloroethane ........................................................ | X | X |  |
| 79–01–6 .......................................... | Trichloroethylene ............................................................... | X | X |  |
| 75–01–4 .......................................... | Vinyl chloride ..................................................................... | .............. | X |  |
| 1330–20–7 ...................................... | Xylene ................................................................................ | X | X | .............. |

      - The following maximum contami- nant levels for synthetic organic con- taminants  apply  to  community  water

systems  and  non-transient,  non-com- munity water systems:

| CAS No. | Contaminant | MCL (mg/l) |
| --- | --- | --- |
| (1) 15972–60–8 ...................................................... | Alachlor ...................................................................... | 0.002 |

#### § 141.62

40 CFR Ch. I (7–1–17 Edition)

| CAS No. | Contaminant | MCL (mg/l) |
| --- | --- | --- |
| (2) 116–06–3 ........................................................... | Aldicarb ...................................................................... | 0.003 |
| (3) 1646–87–3 ......................................................... | Aldicarb sulfoxide ...................................................... | 0.004 |
| (4) 1646–87–4 ......................................................... | Aldicarb sulfone ......................................................... | 0.002 |
| (5) 1912–24–9 ........................................................ | Atrazine ..................................................................... | 0.003 |
| (6) 1563–66–2 ........................................................ | Carbofuran ................................................................. | 0.04 |
| (7) 57–74–9 ............................................................ | Chlordane .................................................................. | 0.002 |
| (8) 96–12–8 ............................................................ | Dibromochloropropane .............................................. | 0.0002 |
| (9) 94–75–7 ............................................................ | 2,4-D .......................................................................... | 0.07 |
| (10) 106–93–4 .......................................................... | Ethylene dibromide .................................................... | 0.00005 |
| (11) 76–44–8 ............................................................ | Heptachlor ................................................................. | 0.0004 |
| (12) 1024–57–3 ........................................................ | Heptachlor epoxide ................................................... | 0.0002 |
| (13) 58–89–9 ............................................................ | Lindane ...................................................................... | 0.0002 |
| (14) 72–43–5 ............................................................ | Methoxychlor ............................................................. | 0.04 |
| (15) 1336–36–3 ........................................................ | Polychlorinated biphenyls .......................................... | 0.0005 |
| (16) 87–86–5 ............................................................ | Pentachlorophenol ..................................................... | 0.001 |
| (17) 8001–35–2 ........................................................ | Toxaphene ................................................................. | 0.003 |
| (18) 93–72–1 ............................................................ | 2,4,5-TP ..................................................................... | 0.05 |
| (19) 50–32–8 ............................................................ | Benzo[a]pyrene ......................................................... | 0.0002 |
| (20) 75–99–0 ............................................................ | Dalapon ..................................................................... | 0.2 |
| (21) 103–23–1 .......................................................... | Di(2-ethylhexyl) adipate ............................................. | 0.4 |
| (22) 117–81–7 .......................................................... | Di(2-ethylhexyl) phthalate .......................................... | 0.006 |
| (23) 88–85–7 ............................................................ | Dinoseb ..................................................................... | 0.007 |
| (24) 85–00–7 ............................................................ | Diquat ........................................................................ | 0.02 |
| (25) 145–73–3 .......................................................... | Endothall .................................................................... | 0.1 |
| (26) 72–20–8 ............................................................ | Endrin ........................................................................ | 0.002 |
| (27) 1071–53–6 ........................................................ | Glyphosate ................................................................ | 0.7 |
| (28) 118–74–1 .......................................................... | Hexacholorbenzene ................................................... | 0.001 |
| (29) 77–47–4 ............................................................ | Hexachlorocyclopentadiene ...................................... | 0.05 |
| (30) 23135–22–0 ...................................................... | Oxamyl (Vydate) ........................................................ | 0.2 |
| (31) 1918–02–1 ........................................................ | Picloram ..................................................................... | 0.5 |
| (32) 122–34–9 .......................................................... | Simazine .................................................................... | 0.004 |
| (33) 1746–01–6 ........................................................ | 2,3,7,8-TCDD (Dioxin) ............................................... | 3 10¥8 |

[56 FR 3593, Jan. 30, 1991, as amended at 56 FR 30280, July 1, 1991; 57 FR 31846, July 17, 1992;

59 FR 34324, July 1, 1994]

##### § 141.62   Maximum  contaminant  levels for inorganic contaminants.

- [Reserved]

- Contaminant

MCL (mg/l)

- Fluoride	4.0

- Asbestos  ..........................   7 Million Fibers/liter (longer

than 10 m).

- Barium	2

- Cadmium	0.005

- Chromium	0.1

- Mercury	0.002

(7) Nitrate ...............................   10 (as Nitrogen)

(8) Nitrite ................................   1 (as Nitrogen)

The maximum contaminant levels for inorganic contaminants specified in paragraphs (b) (2)–(6), (b)(10), and (b) (11)–(16) of this section apply to com- munity water systems and non-tran- sient, non-community  water  systems. The maximum contaminant level spec- ified in paragraph (b)(1) of this section only applies to community water sys- tems.  The  maximum  contaminant  lev- els specified in (b)(7), (b)(8), and (b)(9) of this  section  apply  to  community water systems; non-transient, non- community water systems; and tran- sient  non-community  water  systems.

| Contaminant | MCL (mg/l) |
| --- | --- |
| (9) Total Nitrate and Nitrite .... | 10 (as Nitrogen) |
| (10) Selenium ........................ | 0.05 |
| (11) Antimony ........................ | 0.006 |
| (12) Beryllium ........................ | 0.004 |
| (13) Cyanide (as free Cya- | 0.2 |
| nide). |  |
| (14) [Reserved]. |  |
| (15) Thallium .......................... | 0.002 |
| (16) Arsenic ........................... | 0.010 |

- The Administrator, pursuant to section 1412 of the Act, hereby identi- fies the following as the best tech- nology, treatment technique, or other means available for achieving compli- ance with the maximum contaminant levels for inorganic contaminants iden- tified in paragraph (b) of this section, except fluoride:

BAT FOR INORGANIC COMPOUNDS LISTED IN

SECTION 141.62(b)

Chemical Name

BAT(s)

Antimony ........................................................	2,7

Arsenic 4  .........................................................    1, 2, 5, 6, 7, 9,

12 5

Asbestos ........................................................	2,3,8

Barium  ...........................................................	5,6,7,9

#### Environmental Protection Agency	§ 141.63

BAT FOR INORGANIC COMPOUNDS LISTED IN

| Chemical Name | BAT(s) |
| --- | --- |
| Beryllium ........................................................ | 1,2,5,6,7 |
| Cadmium ....................................................... | 2,5,6,7 |
| Chromium ...................................................... | 2,5,6 2,7 |
| Cyanide .......................................................... | 5,7,13 |
| Mercury .......................................................... | 2 1,4,6 1,7 1 |
| Nickel ............................................................. | 5,6,7 |
| Nitrate ............................................................ | 5,7,9 |
| Nitrite ............................................................. | 5,7 |
| Selenium ........................................................ | 1,2 3,6,7,9 |
| Thallium ......................................................... | 1,5 |

SECTION 141.62(b)—Continued

SMALL SYSTEM COMPLIANCE TECHNOLOGIES (SSCTS) 1  FOR ARSENIC 2—Continued

| Small system compliance technology | Affordable for listed small system categories 3 |
| --- | --- |
| Reverse Osmosis (Point-of- Use) 4. | All size categories. |

1 BAT only if influent Hg concentrations 10g/1.

2 BAT for Chromium III only.

3 BAT for Selenium IV only.

4 BATs for Arsenic V. Pre-oxidation may be required to con- vert Arsenic III to Arsenic V.

5 To obtain high removals, iron to arsenic ratio must be at

least 20:1.

Key to BATS in Table

1  =  Activated  Alumina

2 = Coagulation/Filtration  (not BAT for  sys- tems <500 service connections)

3 = Direct and Diatomite Filtration 4 = Granular Activated Carbon

5 = Ion Exchange

6  =  Lime  Softening  (not  BAT  for  systems

<500 service connections) 7 = Reverse Osmosis

8 = Corrosion Control 9  =  Electrodialysis

10 = Chlorine

11  =  Ultraviolet

12  =  Oxidation/Filtration

13 = Alkaline Chlorination (pH 8.5)

- The Administrator, pursuant to section 1412 of the Act, hereby identi- fies in  the  following  table the  afford- able   technology,   treatment   technique, or other means available to systems serving 10,000 persons or fewer for achieving compliance with  the  max- imum  contaminant  level  for  arsenic:

Small system compliance	Affordable for listed small technology		system categories 3

Activated Alumina (central-

ized).

Activated Alumina (Point-of- Use) 4.

Coagulation/Filtration 5  ........... Coagulation-assisted Micro-

filtration.

Electrodialysis reversal 6 ........ Enhanced coagulation/filtra-

tion.

Enhanced lime softening (pH>10.5).

Ion Exchange .........................

Lime Softening 5   ....................

Oxidation/Filtration 7  ............... Reverse Osmosis (central-

ized) 6.

All size categories.

All size categories.

501–3,300, 3,301–10,000.

501–3,300, 3,301–10,000.

501–3,300, 3,301–10,000.

All size categories All size categories.

All size categories. 501–3,300, 3,301–10,000.

All size categories. 501–3,300, 3,301–10,000.

SMALL SYSTEM COMPLIANCE TECHNOLOGIES (SSCTS) 1 FOR ARSENIC 2

1 Section 1412(b)(4)(E)(ii) of SDWA specifies that SSCTs must be affordable and technically feasible for small systems.

2 SSCTs for Arsenic V. Pre-oxidation may be required to convert Arsenic III to Arsenic V.

3 The Act (ibid.) specifies three categories of small systems:

- those serving 25 or more, but fewer than 501, (ii) those serving more than 500, but fewer than 3,301, and (iii) those serving more than 3,300, but fewer than 10,001.

4 When POU or POE devices are used for compliance, pro- grams to ensure proper long-term operation, maintenance, and monitoring must be provided by the water system to en- sure adequate performance.

5 Unlikely to be installed solely for arsenic removal. May re- quire pH adjustment to optimal range if high removals are needed.

6 Technologies reject a large volume of water—may not be appropriate for areas where water quantity may be an issue.

7 To obtain high removals, iron to arsenic ratio must be at least 20:1.

[56  FR 3594,  Jan. 30,  1991,  as  amended  at 56

FR 30280,  July 1,  1991;  57  FR 31847,  July 17,

1992;  59  FR 34325,  July 1,  1994;  60  FR 33932,

June 29, 1995; 66 FR 7063, Jan. 22, 2001; 68 FR

14506, Mar. 25, 2003; 69 FR 38855, June 29, 2004]

##### § 141.63 Maximum contaminant levels (MCLs) for microbiological contami- nants.

  - Until March 31, 2016, the total coliform MCL is based on the presence or absence of total coliforms in a sam- ple, rather than coliform density.

- For a system that collects at least 40 samples per month, if no more than

5.0 percent  of the  samples collected during a month are total coliform-posi- tive, the system is in compliance  with the MCL for total coliforms.

- For a system that collects fewer than 40 samples per month, if no more than one sample collected during a month is total coliform-positive, the system is in compliance with the  MCL for  total  coliforms.

  - Until March  31, 2016,  any fecal coliform-positive repeat sample or E. coli-positive repeat sample, or any total coliform-positive repeat sample following a fecal coliform-positive or E. coli-positive routine sample, con- stitutes a violation of the MCL for total coliforms. For purposes of the public notification requirements in subpart Q of this part, this is a viola- tion that may pose an acute risk to health.

  - Beginning April 1, 2016, a system is  in  compliance  with  the  MCL  for  E.

#### § 141.64

coli for samples taken under the provi- sions of subpart Y of this part  unless any of the conditions identified in paragraphs (c)(1) through (c)(4) of this section occur. For purposes of the pub- lic notification requirements in  sub- part Q of this part, violation  of the MCL may pose an acute risk to health.

    - The system has an E. coli-positive repeat sample following a total coli- form-positive routine sample.

    - The system has a total coliform- positive repeat sample following an E. coli-positive routine sample.

    - The system fails to take all re- quired repeat samples following an E. coli-positive routine sample.

    - The system fails to test for E. coli when any repeat sample tests positive for total coliform.

  - Until March 31, 2016, a public water system must determine compli- ance with the MCL  for  total  coliforms in paragraphs (a) and (b) of this section for each month in which it is required to monitor for total coliforms. Begin- ning April 1, 2016, a public water sys- tem must determine compliance with the MCL for E. coli in paragraph (c) of this section for each month in which it is required to monitor for total coli- forms.

  - The Administrator, pursuant to section 1412 of the Act, hereby identi- fies the following as the best tech- nology, treatment techniques, or other means available for achieving compli- ance with the maximum contaminant level  for  total  coliforms  in  paragraphs

- and (b) of this section and for achieving compliance with the max- imum contaminant level for E. coli in paragraph (c) of this section:

  - Protection of wells from fecal con- tamination by appropriate placement and construction;

  - Maintenance of a disinfectant re- sidual throughout the distribution sys- tem;

  - Proper maintenance of the dis- tribution system including appropriate pipe replacement and repair proce- dures, main flushing programs, proper operation and maintenance of storage tanks and reservoirs, cross connection control, and continual maintenance of positive water pressure in all parts  of the distribution system;

#### 40 CFR Ch. I (7–1–17 Edition)

  - Filtration and/or disinfection of surface water, as described in subparts H, P, T, and W of this part, or disinfec- tion of ground water, as described in subpart S of this part, using strong oxidants such as chlorine, chlorine di- oxide, or ozone; and

  - For systems using ground water, compliance with the requirements of an EPA-approved State Wellhead Pro- tection Program developed and imple- mented under section 1428 of the SDWA.

  - The Administrator, pursuant to section 1412 of the Act, hereby identi- fies the technology, treatment tech- niques, or other means available iden- tified in paragraph (e) of this section as affordable technology, treatment tech- niques, or other means available to systems serving 10,000 or fewer people for achieving compliance with the maximum contaminant level for total coliforms in paragraphs (a) and (b) of this section and for  achieving  compli- ance with the maximum contaminant level for E. coli in paragraph (c) of this section.

[78 FR 10347, Feb. 13, 2013]

##### § 141.64   Maximum  contaminant  levels for disinfection byproducts.

- Bromate and chlorite. The max- imum contaminant levels (MCLs) for bromate and chlorite are as follows:

| Disinfection byproduct | MCL (mg/L) |
| --- | --- |
| Bromate ............................................................. Chlorite .............................................................. | 0.010 1.0 |

  - Compliance dates for CWSs and NTNCWSs. Subpart H systems serving 10,000 or more persons  must  comply with this paragraph (a) beginning Jan- uary 1, 2002. Subpart H systems serving fewer than 10,000 persons and systems using only ground water not under the direct influence of surface water must comply with this paragraph (a) begin- ning January 1, 2004.

  - The Administrator, pursuant to section 1412 of the Act, hereby identi- fies the following as the best tech- nology, treatment techniques, or other means available for achieving compli- ance with the maximum contaminant levels for bromate and chlorite identi- fied in this paragraph (a):

#### Environmental Protection Agency	§ 141.65

| Disinfection byproduct | Best available technology |
| --- | --- |
| Bromate .... Chlorite ...... | Control of ozone treatment process to reduce production of bromate Control of treatment processes to reduce dis- infectant demand and control of disinfection treatment processes to reduce disinfectant levels |
| Disinfection byprod- uct | Best available technology |
| Total trihalomethanes (TTHM) and Haloacetic acids (five) (HAA5). | Enhanced coagulation or enhanced softening, plus GAC10; or nanofiltra- tion with a molecular weight cutoff 1000 Daltons; or GAC20 |

ance with the maximum contaminant levels for TTHM and HAA5 identified in this paragraph (b)(2) for all systems that disinfect their source water:

- TTHM and HAA5. (1) Subpart L— RAA compliance. (i) Compliance dates. Subpart H systems serving 10,000  or more persons must comply with this paragraph (b)(1) beginning January 1, 2002. Subpart H systems serving fewer than 10,000 persons and systems using only ground water not under the direct influence of surface water must comply with this paragraph (b)(1) beginning January 1, 2004. All systems must  com- ply with these MCLs until the date specified   for   subpart   V   compliance   in

| Disinfection byproduct | MCL (mg/L) |
| --- | --- |
| Total trihalomethanes (TTHM) .......................... Haloacetic acids (five) (HAA5) .......................... | 0.080 0.060 |

§ 141.620(c).

| Disinfection byprod- uct | Best available technology |
| --- | --- |
| Total trihalomethanes (TTHM) and Haloacetic acids (five) (HAA5). | Systems serving 10,000: Improved distribution system and storage tank management to reduce residence time, plus the use of chloramines for disinfectant residual maintenance Systems serving <10,000: Improved distribution system and storage tank management to reduce residence time |

(iii) The Administrator, pursuant to section 1412 of the Act, hereby identi- fies the following as the best tech- nology, treatment techniques, or other means available for achieving compli- ance with the maximum contaminant levels for TTHM and HAA5 identified in this paragraph (b)(2) for consecutive systems and applies only to the dis- infected water  that  consecutive  sys- tems buy or otherwise receive:

| Disinfection byproduct | Best available technology |
| --- | --- |
| Total trihalomethanes (TTHM) and Haloacetic acids (five) (HAA5). | Enhanced coagulation or en- hanced softening or GAC10, with chlorine as the primary and residual disinfectant |

(ii) The Administrator, pursuant to section 1412 of the Act, hereby identi- fies the following as the best tech- nology, treatment techniques, or other means available for achieving compli- ance with the maximum contaminant levels for TTHM and HAA5 identified in this paragraph (b)(1):

[71 FR 478, Jan. 4, 2006]

##### § 141.65   Maximum   residual   disinfect- ant levels.

| Disinfectant residual | MRDL (mg/L) |
| --- | --- |
| Chlorine ................................................ Chloramines ......................................... Chlorine dioxide ................................... | 4.0 (as Cl2). 4.0 (as Cl2). 0.8 (as ClO2). |

Maximum   residual   disinfectant levels (MRDLs) are as follows:

(2) Subpart V—LRAA compliance. (i) Compliance dates. The subpart V  MCLs for TTHM and HAA5 must be complied with as a locational running annual av- erage at each monitoring location be- ginning the date specified for subpart V compliance in § 141.620(c).

| Disinfection byproduct | MCL (mg/L) |
| --- | --- |
| Total trihalomethanes (TTHM) .......................... Haloacetic acids (five) (HAA5) .......................... | 0.080 0.060 |

(ii) The Administrator, pursuant to section 1412 of the Act, hereby identi- fies the following as the best tech- nology, treatment techniques, or other means  available  for  achieving  compli-

- Compliance dates—(1) CWSs and NTNCWSs. Subpart H systems serving 10,000 or more persons  must  comply with this section beginning January 1, 2002. Subpart H systems serving fewer than 10,000 persons and systems using only ground water not under the direct influence of surface water must comply with this subpart beginning January 1, 2004.

- Transient NCWSs. Subpart H sys- tems serving 10,000 or more persons and using  chlorine  dioxide  as  a  disinfectant

#### § 141.66

or oxidant must comply with the chlo- rine  dioxide  MRDL   beginning   January 1, 2002. Subpart H systems serving fewer than 10,000 persons and using chlorine dioxide as a disinfectant or oxidant and systems using only ground water not under the direct influence of surface water and using chlorine diox- ide as a disinfectant or oxidant must comply  with  the  chlorine   dioxide MRDL  beginning  January  1,  2004.

- The Administrator, pursuant to Section 1412 of the Act, hereby identi- fies the following as the best tech- nology, treatment techniques, or other means available for achieving compli- ance with the maximum residual dis- infectant  levels  identified  in  paragraph

  - of this section: control of treatment processes to reduce disinfectant de- mand and control of disinfection treat- ment processes to reduce disinfectant levels.

[63 FR 69465, Dec. 16, 1998, as amended at 66

FR 3776, Jan. 16, 2001]

##### § 141.66   Maximum  contaminant  levels for radionuclides.

    - [Reserved]

    - MCL  for  combined  radium-226  and

-228. The maximum contaminant level for combined radium-226 and radium- 228 is 5 pCi/L. The combined radium-226 and radium-228 value is determined by the addition of the results of the anal- ysis for radium-226 and the analysis for radium-228.

    - MCL for gross alpha particle activ- ity (excluding radon and uranium). The maximum contaminant level for gross alpha particle activity (including ra- dium-226 but excluding radon and ura- nium) is 15 pCi/L.

    - MCL for beta particle and photon radioactivity. (1) The average annual concentration of beta particle and pho- ton radioactivity from man-made radionuclides in drinking water must not produce an annual dose equivalent to the total body or any internal organ greater than 4 millirem/year (mrem/ year).

(2) Except for the radionuclides listed in table A, the concentration of man- made radionuclides causing 4 mrem total body or organ dose equivalents must be calculated on the basis of 2 liter per day drinking water intake using  the  168  hour  data  list  in  ‘‘Max-

#### 40 CFR Ch. I (7–1–17 Edition)

imum Permissible Body Burdens and Maximum Permissible Concentrations of Radionuclides in Air and in  Water for Occupational Exposure,’’ NBS (Na- tional Bureau of Standards) Handbook

69  as amended August 1963,  U.S. De- partment of Commerce. This incorpo- ration by reference was approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies of this document are available from the National Tech- nical  Information  Service,  NTIS  ADA 280 282, U.S. Department of Commerce, 5285 Port Royal Road, Springfield, Vir- ginia 22161. The toll-free number is 800– 553–6847. Copies may be inspected at EPA’s  Drinking  Water  Docket,  401  M Street, SW., Washington, DC 20460; or at the National Archives and Records Administration  (NARA).  For  informa- tion  on  the  availability  of  this  mate- rial at NARA, call 202–741–6030.   If    two    or    more radionuclides are present, the sum of their  annual  dose  equivalent  to  the total body or to any organ shall not ex- ceed 4 mrem/year.

TABLE A—AVERAGE ANNUAL CONCENTRATIONS ASSUMED TO PRODUCE: A TOTAL BODY OR ORGAN DOSE OF 4 MREM/YR

| 1. Radionuclide ..... | Critical organ ........ | pCi per liter |
| --- | --- | --- |
| 2. Tritium .............. | Total body ............ | 20,000 |
| 3. Strontium-90 ..... | Bone Marrow ........ | 8 |

    - MCL for uranium. The maximum contaminant level for uranium is 30 g/ L.

    - Compliance dates. (1) Compliance dates for combined radium-226 and -228, gross  alpha  particle  activity,   gross beta particle and photon radioactivity, and uranium: Community water sys- tems must comply with the  MCLs  list- ed in paragraphs (b), (c), (d), and (e) of this section beginning December 8, 2003 and compliance shall be determined in accordance  with  the  requirements  of

§§ 141.25 and 141.26. Compliance with re- porting requirements for the radio- nuclides under appendix A to subpart O and appendices A and B to subpart Q is required on December 8, 2003.

(2)  [Reserved]

#### Environmental Protection Agency	§ 141.66

    - Best available technologies (BATs) for radionuclides. The Administrator, pursuant to section 1412 of the Act, hereby identifies as indicated  in the following   table   the   best   technology

available for achieving  compliance with the maximum contaminant levels for combined radium-226 and -228, ura- nium, gross alpha particle activity, and beta particle and photon radioactivity.

TABLE B—BAT FOR COMBINED RADIUM-226 AND RADIUM-228, URANIUM, GROSS ALPHA PARTICLE ACTIVITY, AND BETA PARTICLE AND PHOTON RADIOACTIVITY

| Contaminant | BAT |
| --- | --- |
| 1. Combined radium-226 and radium-228 .................................. 2. Uranium ................................................................................... 3. Gross alpha particle activity (excluding Radon and Uranium) 4. Beta particle and photon radioactivity ..................................... | Ion exchange, reverse osmosis, lime softening. Ion exchange, reverse osmosis, lime softening, coagulation/fil- tration. Reverse osmosis. Ion exchange, reverse osmosis. |

    - Small systems compliance technologies list for radionuclides.

TABLE C—LIST OF SMALL SYSTEMS COMPLIANCE TECHNOLOGIES FOR RADIONUCLIDES AND

LIMITATIONS TO USE

| Unit technologies | Limitations (see foot- notes) | Operator skill level required 1 | Raw water quality range and considerations. 1 |
| --- | --- | --- | --- |
| 1. Ion exchange (IE) ............................. 2. Point of use (POU 2) IE .................... 3. Reverse osmosis (RO) ..................... 4. POU 2 RO ......................................... 5. Lime softening .................................. 6. Green sand filtration ......................... Co-precipitation with Barium sulfate Electrodialysis/electrodialysis rever- sal. Pre-formed hydrous Manganese oxide filtration. 10. Activated alumina ........................... 11. Enhanced coagulation/filtration ...... | (a) (b) (c) (b) (d) (e) (f) .................... (g) (a), (h) (i) | Intermediate ................................... Basic .............................................. Advanced ....................................... Basic .............................................. Advanced ....................................... Basic. Intermediate to Advanced .............. Basic to Intermediate ..................... Intermediate ................................... Advanced ....................................... Advanced ....................................... | All ground waters. All ground waters. Surface waters usually require pre- filtration. Surface waters usually require pre- filtration. All waters. Ground waters with suitable water quality. All ground waters. All ground waters. All ground waters; competing anion concentrations may affect regeneration frequency. Can treat a wide range of water qualities. |

1 National Research Council (NRC). Safe Water from Every Tap: Improving Water Service to Small Communities. National Academy Press. Washington, D.C. 1997.

2 A POU, or ‘‘point-of-use’’ technology is a treatment device installed at a single tap used for the purpose of reducing contami- nants in drinking water at that one tap. POU devices are typically installed at the kitchen tap. See the April 21, 2000 NODA for more details.

Limitations Footnotes: Technologies for Radionuclides:

a The regeneration solution contains high concentrations of the contaminant ions. Disposal options should be carefully consid- ered before choosing this technology.

b When POU devices are used for compliance, programs for long-term operation, maintenance, and monitoring must be pro- vided by water utility to ensure proper performance.

c Reject water disposal options should be carefully considered before choosing this technology. See other RO limitations de- scribed in the SWTR Compliance Technologies Table.

d The combination of variable source water quality and the complexity of the water chemistry involved may make this tech- nology too complex for small surface water systems.

e Removal efficiencies can vary depending on water quality.

f This technology may be very limited in application to small systems. Since the process requires static mixing, detention ba- sins, and filtration, it is most applicable to systems with sufficiently high sulfate levels that already have a suitable filtration treat- ment train in place.

g This technology is most applicable to small systems that already have filtration in place.

h Handling of chemicals required during regeneration and pH adjustment may be too difficult for small systems without an ade- quately trained operator.

i Assumes modification to a coagulation/filtration process already in place.

TABLE D—COMPLIANCE TECHNOLOGIES BY SYSTEM SIZE CATEGORY FOR RADIONUCLIDE NPDWR’S

| Contaminant | Compliance technologies 1 for system size categories (population served) | 3,300–10,000 |
| --- | --- | --- |
|  | 25–500 | 501–3,300 |  |
| 1. Combined radium-226 and radium-228 | 1, 2, 3, 4, 5, 6, 7, 8, 9 ..... | 1, 2, 3, 4, 5, 6, 7, 8, 9 ..... | 1, 2, 3, 4, 5, 6, 7. 8, 9. |

#### § 141.70

40 CFR Ch. I (7–1–17 Edition)

TABLE D—COMPLIANCE TECHNOLOGIES BY SYSTEM SIZE CATEGORY FOR RADIONUCLIDE

NPDWR’S—Continued

| Contaminant | Compliance technologies 1 for system size categories (population served) | 3,300–10,000 |
| --- | --- | --- |
|  | 25–500 | 501–3,300 |  |
| 2. Gross alpha particle activity ................... | 3, 4 ................................... | 3, 4 ................................... | 3, 4. |
| 3. Beta particle activity and photon activity | 1, 2, 3, 4 .......................... | 1, 2, 3, 4 .......................... | 1, 2, 3, 4. |
| 4. Uranium .................................................. | 1, 2, 4, 10, 11 .................. | 1, 2, 3, 4, 5, 10, 11 .......... | 1, 2, 3, 4, 5, 10, 11. |

NOTE: 1 Numbers correspond to those technologies found listed in the table C of 141.66(h).

[65 FR 76748, Dec. 7, 2000]

# Subpart H—Filtration and Disinfection

SOURCE:  54  FR  27527,  June  29,  1989,  unless

otherwise noted.

##### § 141.70   General requirements.

- The requirements of  this  subpart H constitute national primary drinking water regulations. These regulations establish criteria under which  filtra- tion is required as a treatment tech- nique for public water systems supplied by a surface water source and public water systems supplied by a ground water source under the direct influence of surface water. In addition, these reg- ulations establish treatment technique requirements in lieu of maximum con- taminant levels for the following con- taminants: Giardia lamblia, viruses, heterotrophic plate count bacteria, Legionella, and turbidity. Each public water system with a surface water source or a ground water source under the direct influence of surface water must provide treatment of that source water that complies with these treat- ment technique requirements. The treatment technique requirements con- sist of installing and properly  oper- ating water treatment processes which reliably  achieve:

  - At least 99.9 percent (3-log) re- moval and/or inactivation of Giardia lamblia cysts between a point where the raw water is not subject to recontami- nation by surface water runoff and a point downstream before or at the first customer; and

  - At least 99.99 percent (4-log) re- moval and/or inactivation of viruses between a point where the raw water is not subject to recontamination by sur-

face  water  runoff  and  a  point  down- stream before or at the first customer.

- A public water system using a surface water source or a ground water source under the direct influence of surface water is considered to be in compliance with the requirements of paragraph (a) of this section if:

  - It meets the requirements for avoiding filtration in § 141.71 and the disinfection requirements in § 141.72(a); or

  - It meets the filtration  require- ments in § 141.73 and the disinfection requirements in § 141.72(b).

- Each public water system using a surface water source or a ground water source under the direct influence of surface water must be operated by qualified personnel who meet the re- quirements specified by the State.

- Additional requirements for systems serving at least 10,000 people. In addition to complying with requirements in this subpart, systems serving at least 10,000 people must also comply with the re- quirements  in  subpart  P  of  this  part.

- Additional requirements for systems serving fewer than 10,000 people. In addi- tion to complying with requirements in this  subpart,  systems  serving  fewer than 10,000 people must  also  comply with the requirements in subpart T of this   part.

[54 FR 27527, June 29, 1989, as amended at 63

FR 69516,  Dec. 16,  1998;  67  FR 1836,  Jan. 14,

2002]

##### § 141.71   Criteria   for   avoiding   filtra- tion.

A public water system that uses a surface water source must meet all of the conditions of paragraphs (a) and (b)

Environmental Protection Agency	§ 141.71

of this section, and is subject to para- graph (c) of this section, beginning De- cember 30, 1991, unless the State has determined,   in   writing   pursuant   to

§ 1412(b)(7)(C)(iii), that filtration is re- quired.  A  public  water   system   that uses a ground water source under the direct influence of surface water must meet all of the conditions of para- graphs (a) and (b) of this section and is subject to paragraph (c) of this section, beginning 18 months after the State  de- termines that it is under the direct in- fluence of surface water, or December 30, 1991, whichever is later, unless the State has determined, in writing pursu- ant to § 1412(b)(7)(C)(iii), that filtration is required. If the State determines in writing pursuant to § 1412(b)(7)(C)(iii) before December 30, 1991, that filtra- tion is required, the system must have installed filtration and meet  the  cri- teria   for   filtered   systems   specified   in

§§ 141.72(b) and 141.73 by June 29, 1993. Within 18  months of the failure of  a system using surface water or a ground water source under the  direct  influence of surface water to meet any one of the requirements of paragraphs (a)  and  (b) of this section or after June 29, 1993, whichever is later, the  system  must have installed filtration and meet the criteria  for  filtered   systems   specified in §§ 141.72(b) and 141.73.

- Source water quality conditions. (1) The fecal coliform concentration must be equal to or less than 20/100 ml, or the total coliform concentration must be equal to or less than 100/100 ml (meas- ured as specified in § 141.74  (a) (1)  and

(2) and (b)(1)), in representative sam- ples of the source water immediately prior to the first or only point of dis- infectant application in at least 90 per- cent of the measurements made for the

6 previous months that the system served water to the public on an ongo- ing basis. If a system measures both fecal and total coliforms, the fecal coli- form criterion, but not the total coli- form criterion, in this paragraph  must be met.

(2) The turbidity  level  cannot  exceed 5 NTU (measured as specified in § 141.74 (a)(1) and (b)(2)) in representative sam- ples of the source water  immediately prior to the first or only point of dis- infectant application  unless:  (i)  the State   determines   that   any   such   event

was caused by circumstances that were unusual and unpredictable; and (ii) as a result of any such event, there have not been more  than two events  in the past 12 months the system served water to the public, or more than five events in the past 120 months the sys- tem served water to the public,  in which the turbidity level exceeded 5 NTU. An ‘‘event’’ is a series of consecu- tive days during which at least one tur- bidity measurement each day exceeds 5 NTU.

- Site-specific conditions. (1)(i) The public water system must meet the re- quirements of § 141.72(a)(1) at least 11 of the 12 previous months that the system served water to the public, on  an  ongo- ing basis, unless the  system  fails  to meet  the  requirements  during  2  of  the

12 previous months that the system served water to the  public,  and  the State determines that at least one of these failures was caused by cir- cumstances that were unusual and un- predictable.

- The public water system must meet the requirements of  § 141.72(a)(2) at all times the system serves  water  to the  public.

- The public water system must meet the requirements of § 141.72(a)(3) at all times the system serves water to the public unless the State determines that any such failure was caused by circumstances that were unusual and unpredictable.

- The public water system must meet the requirements of § 141.72(a)(4) on an ongoing basis unless the State determines that failure to meet these requirements was not caused by a defi- ciency in  treatment  of  the  source water.

- The public water system must maintain a watershed control program which minimizes the potential for con- tamination by Giardia lamblia cysts and viruses in the source water. The State must determine whether the watershed control program is adequate to meet this goal. The adequacy  of  a  program to limit potential contamination by Giardia lamblia cysts and viruses must be based on: the comprehensiveness of the watershed review; the effectiveness of   the   system’s   program   to   monitor

#### § 141.71

and control detrimental activities oc- curring in the watershed; and the ex- tent to which the water system has maximized land ownership and/or con- trolled land use within the watershed. At a minimum, the watershed control program must:

  - Characterize the watershed hy- drology and land ownership;

  - Identify watershed characteris- tics and activities which may have an adverse effect on source water quality; and

  - Monitor the occurrence of activi- ties which may have an  adverse  effect on source water quality.

The public water system must dem- onstrate through ownership and/or written agreements with landowners within the watershed that it can con- trol all human activities  which  may have an adverse impact on the micro- biological quality of the source water. The public water system must  submit an annual report to the State that identifies any special concerns about the watershed and how they are being handled; describes activities in the wa- tershed that affect water quality; and projects what adverse activities are ex- pected to occur in the future and de- scribes how the public water system expects to address them. For systems using a ground water source under the direct influence of surface water, an approved wellhead protection program developed under section 1428 of the Safe Drinking Water Act may be used, if the State deems it appropriate, to meet these requirements.

- The public water system must be subject to an annual on-site inspection to assess the watershed control pro- gram and disinfection treatment proc- ess. Either the State or a party ap- proved by the State must conduct the on-site inspection. The inspection must be conducted by competent individuals such as sanitary and civil engineers, sanitarians, or technicians who have experience and knowledge about the operation and maintenance of a public water system, and who have a sound understanding of public health prin- ciples and waterborne diseases. A re- port of the on-site inspection summa- rizing all findings must be prepared every year.  The  on-site  inspection must   indicate   to   the   State’s   satisfac-

#### 40 CFR Ch. I (7–1–17 Edition)

tion that the watershed control pro- gram and disinfection treatment proc- ess are adequately designed and main- tained. The on-site inspection must in- clude:

- A review of the effectiveness of the watershed control program;

- A review of the physical condi- tion of the source intake and how well it is protected;

- A review of the system’s equip- ment maintenance program to ensure there is low probability for failure of the disinfection process;

- An inspection of the disinfection equipment for physical deterioration;

- A review of operating procedures;

- A review of data records to en- sure that all required tests are being conducted and recorded and disinfec- tion is effectively practiced; and

- Identification of any improve- ments which are needed in the equip- ment, system maintenance and oper- ation, or data collection.

- The public water system must not have been identified as a source of a waterborne disease outbreak, or if it has been so identified, the system must have been modified sufficiently to pre- vent another such occurrence, as deter- mined by the State.

- The public water system must comply with the maximum contami- nant level (MCL) for total coliforms in

§ 141.63(a) and (b) and the MCL for E. coli in § 141.63(c) at least 11 months of the 12 previous months that the system served water to the public, on an ongo- ing basis, unless the State determines that failure to meet this requirement was not caused by a deficiency in treat- ment of the source water.

- The public water system must comply with the requirements for trihalomethanes in §§ 141.12 and 141.30 until December 31,  2001. After Decem- ber 31, 2001, the system must comply with the requirements for total trihalomethanes,  haloacetic   acids (five), bromate, chlorite, chlorine, chloramines, and chlorine dioxide in subpart L of this part.

- Treatment technique violations. (1) A system that (i) fails to meet any one of the criteria in paragraphs (a) and (b) of this section and/or which the State has determined that filtration is re- quired,      in      writing      pursuant      to

#### Environmental Protection Agency	§ 141.72

§ 1412(b)(7)(C)(iii), and (ii) fails to in- stall filtration by the date specified  in the introductory paragraph of this sec- tion is in violation of a treatment tech- nique requirement.

- A system that has not installed filtration is in violation of a treatment technique requirement if:

  - The turbidity level (measured as specified in § 141.74(a)(1) and (b)(2)) in a representative sample of  the  source water immediately prior to the first or only point of disinfection application exceeds 5 NTU; or

  - The system is identified as a source of a waterborne disease out- break.

[54 FR 27527, June 29, 1989, as amended at 63

FR 69516,  Dec. 16,  1998;  66  FR 3776,  Jan. 16,

2001; 69 FR 38855, June 29, 2004; 78 FR 10347,

Feb. 13, 2013]

##### § 141.72   Disinfection.

A public water system that uses a surface water source and does not pro- vide filtration  treatment  must  provide the disinfection treatment specified in paragraph (a) of this section beginning December 30, 1991, unless the State de- termines that filtration is required in writing pursuant to § 1412 (b)(7)(C)(iii). A public water system  that uses a ground water source under the direct influence of surface water and does not provide filtration treatment must  pro- vide disinfection treatment specified in paragraph (a) of this section beginning December 30, 1991, or 18 months  after the State determines that the ground water source is under the influence of surface water,  whichever  is  later,  un- less the State has determined that fil- tration is required in  writing  pursuant to § 1412(b)(7)(C)(iii). If the State has determined that  filtration  is  required, the system must comply with any in- terim  disinfection  requirements  the State deems necessary  before  filtration is installed. A system that uses a sur- face water source that provides filtra- tion treatment must provide the dis- infection treatment specified in para- graph  (b)  of  this   section   beginning June 29, 1993, or beginning when filtra- tion is installed, whichever is later. A system that uses a ground water source under the direct influence of surface water and  provides  filtration  treat- ment   must   provide   disinfection   treat-

ment as specified in paragraph (b) of this section by June 29, 1993, or begin- ning when filtration is installed, whichever is later. Failure to meet any requirement of this section after the applicable date specified in this intro- ductory paragraph is a treatment tech- nique  violation.

- Disinfection requirements for public water systems that do not provide filtra- tion. Each public water system that does not provide filtration treatment must provide disinfection treatment as follows:

  - The disinfection  treatment  must be sufficient to ensure at least 99.9 per- cent (3-log) inactivation of Giardia lamblia cysts and 99.99 percent (4-log) inactivation of viruses, every day the system serves water to the public, ex- cept any one day each month. Each day a  system  serves  water  to  the   public, the public water system must calculate the CT value(s) from the system’s treatment parameters, using the proce- dure specified in § 141.74(b)(3), and de- termine whether this value(s) is suffi- cient to achieve the specified inactiva- tion rates for Giardia lamblia cysts and viruses. If a system uses a disinfectant other than chlorine, the system may demonstrate to the State, through the use of a State-approved protocol for on- site disinfection challenge studies or other information satisfactory to the State,  that  CT99.9  values  other   than those  specified  in  tables  2.1  and  3.1  in

§ 141.74(b)(3) or other operational pa- rameters are adequate to demonstrate that the system is achieving minimum inactivation rates required  by  para- graph (a)(1) of this section.

  - The disinfection system must have either (i) redundant components, including an auxiliary power supply with automatic start-up and alarm to ensure that disinfectant application is maintained continuously while  water is being delivered to the distribution system, or (ii) automatic shut-off of de- livery of water to the distribution sys- tem whenever there is less than 0.2 mg/ l of residual disinfectant concentration in the water. If the State determines that automatic shut-off would cause unreasonable risk to health or inter- fere with fire protection, the system must comply with paragraph (a)(2)(i) of this section.

#### § 141.72

  - The residual disinfectant con- centration in the water entering the distribution system, measured as speci- fied in § 141.74 (a)(2) and (b)(5), cannot be less than 0.2 mg/l for more than 4 hours.

(4)(i) The residual disinfectant con- centration in the distribution system, measured as total chlorine, combined chlorine, or chlorine dioxide, as speci- fied in § 141.74 (a)(2) and (b)(6), cannot be undetectable  in more  than 5  percent of the samples each month, for any two consecutive months that the system serves water to the public. Water in the distribution	system	with	a heterotrophic   bacteria   concentration less than or equal  to  500/ml,  measured as heterotrophic plate count (HPC) as specified in  § 141.74(a)(1),  is  deemed  to have a  detectable  disinfectant  residual for purposes of determining compliance with this requirement. Thus, the value ‘‘V’’ in the following formula cannot exceed 5 percent in one month, for  any two  consecutive  months.

V c d e 100 a b

where:

a = number of instances where the residual disinfectant concentration is measured;

b = number of instances where the residual disinfectant concentration is not meas- ured but heterotrophic bacteria plate count (HPC) is measured;

c = number of instances where the residual disinfectant concentration is measured but not detected and no HPC is meas- ured;

d = number of instances where the residual disinfectant concentration is measured but not detected and where the HPC is

>500/ml; and

e = number of instances where the residual disinfectant concentration is not meas- ured and HPC is >500/ml.

(ii) If the State determines, based on site-specific considerations, that a sys- tem has no means for having a sample transported and analyzed for HPC by a certified laboratory under the requisite time and temperature conditions speci- fied by § 141.74(a)(1) and that the sys- tem is providing adequate  disinfection in the distribution system, the require- ments of paragraph (a)(4)(i) of this sec- tion do not apply to that system.

- Disinfection requirements for public water  systems  which  provide  filtration.

#### 40 CFR Ch. I (7–1–17 Edition)

Each public water system that provides filtration treatment must provide dis- infection treatment as follows.

- The disinfection treatment must be sufficient to ensure that the total treatment processes of that system achieve at least 99.9 percent (3-log) in- activation and/or removal of Giardia lamblia cysts and at least 99.99 percent (4-log) inactivation and/or removal of viruses, as determined by the State.

- The residual disinfectant con- centration in the water entering the distribution system, measured as speci- fied in § 141.74 (a)(2) and (c)(2), cannot be less than 0.2 mg/l for more than 4 hours.

(3)(i) The residual disinfectant con- centration in the distribution system, measured as total chlorine, combined chlorine, or chlorine dioxide, as speci- fied in § 141.74 (a)(2) and (c)(3), cannot be undetectable  in more  than 5  percent of the samples each month, for any two consecutive months that the system serves water to the public. Water in the distribution	system	with	a heterotrophic   bacteria   concentration less than or equal  to  500/ml,  measured as heterotrophic plate count (HPC) as specified in  § 141.74(a)(1),  is  deemed  to have a  detectable  disinfectant  residual for purposes of determining compliance with this requirement. Thus, the value ‘‘V’’ in the following formula cannot exceed 5 percent in one month, for  any two  consecutive  months.

## V c d e 100 a b

where:

a = number of instances where the residual disinfectant concentration is measured;

b = number of instances where the residual disinfectant concentration is not meas- ured but heterotrophic bacteria plate count (HPC) is measured;

c = number of instances where the residual disinfectant concentration is measured but not detected and no HPC is meas- ured;

d = number of instances where no residual disinfectant  concentration  is  detected and where the HPC is >500/ml; and

e = number of instances where the residual disinfectant concentration is not meas- ured and HPC is >500/ml.

(ii) If the State determines, based on site-specific considerations, that a sys- tem has no means for having a sample

#### Environmental Protection Agency	§ 141.73

transported and analyzed for HPC by a certified laboratory under the requisite time and temperature conditions speci- fied in § 141.74(a)(1) and that the system is providing  adequate  disinfection  in the distribution system, the require- ments of paragraph (b)(3)(i) of this sec- tion do not apply.

[54 FR 27527, June 29, 1989, as amended at 69

FR 38855, June 29, 2004]

##### § 141.73   Filtration.

A public water system that uses a surface water source or a ground water source under the direct influence of surface water, and does not meet all of the criteria in § 141.71 (a) and (b) for avoiding filtration, must provide treat- ment consisting of both disinfection, as specified in § 141.72(b), and filtration treatment which complies with the re- quirements of paragraph (a), (b), (c), (d), or (e) of this section by June 29, 1993, or within 18 months of the failure to meet any one of the criteria for avoiding filtration in § 141.71 (a) and (b), whichever is later. Failure to meet any requirement of this section after the date specified in this introductory paragraph is a treatment technique violation.

- Conventional filtration treatment or direct filtration. (1) For systems using conventional filtration or direct filtra- tion, the turbidity level of representa- tive samples of a system’s filtered water must be less than or equal to 0.5 NTU in at least 95 percent of the meas- urements taken each month, measured as specified in § 141.74 (a)(1) and (c)(1), except that if  the  State  determines that the system is capable of achieving at least 99.9 percent removal and/or in- activation of Giardia lamblia cysts at some turbidity level higher than 0.5 NTU in at least 95 percent of the meas- urements taken each month, the State may substitute this higher turbidity limit for that system. However, in no case may the State approve a turbidity limit that allows more than 1 NTU in more than 5 percent of the samples taken each month, measured as speci- fied in § 141.74 (a)(1) and (c)(1).

  - The turbidity level of representa- tive  samples  of  a  system’s  filtered water must at no time exceed 5 NTU, measured as specified in § 141.74 (a)(1) and (c)(1).

  - Beginning January 1, 2002, sys- tems serving at least 10,000 people must meet    the    turbidity    requirements    in

§ 141.173(a).

  - Beginning January 1, 2005, sys- tems serving fewer than 10,000 people must  meet  the   turbidity   requirements in §§ 141.550 through 141.553.

- Slow sand filtration. (1) For sys- tems using slow sand filtration, the turbidity level of representative sam- ples of a system’s filtered  water  must be less than or equal to 1 NTU in  at least 95 percent of the measurements taken each month, measured as speci- fied in § 141.74 (a)(1) and (c)(1), except that if the State determines there is no significant interference with disinfec- tion at a higher  turbidity  level,  the State may substitute this higher tur- bidity  limit  for  that  system.

(2) The turbidity level of representa- tive  samples  of  a  system’s  filtered water must at no time exceed 5 NTU, measured as specified in § 141.74 (a)(1) and (c)(1).

- Diatomaceous earth filtration. (1) For systems using diatomaceous earth filtration, the turbidity level of rep- resentative samples of a system’s fil- tered water must be less than or equal to 1 NTU in at least 95 percent of the measurements taken each month, measured as specified in § 141.74 (a)(1) and (c)(1).

(2) The turbidity level of representa- tive  samples  of  a  system’s  filtered water must at no time exceed 5 NTU, measured as specified in § 141.74 (a)(1) and (c)(1).

- Other filtration technologies. A pub- lic water system  may use a  filtration technology not listed in paragraphs (a) through (c) of this section if it dem- onstrates to the State, using  pilot plant studies or other means, that the alternative filtration technology, in combination with disinfection treat- ment that meets the requirements of

§ 141.72(b), consistently achieves 99.9 percent removal and/or inactivation of Giardia lamblia cysts and 99.99 percent removal and/or inactivation of viruses. For a system that makes this dem- onstration, the requirements of para- graph (b) of this section apply. Begin- ning  January  1,  2002,  systems  serving

#### § 141.74

at least 10,000 people must meet the re- quirements for other filtration tech- nologies in § 141.173(b). Beginning Janu- ary 14, 2005, systems serving fewer than 10,000 people must meet the require- ments  for  other  filtration   technologies in § 141.550 through 141.553.

[54 FR 27527, June 29, 1989, as amended at 63

FR 69516,  Dec. 16,  1998;  66  FR 3776,  Jan. 16,

2001;  67  FR 1836,  Jan. 14,  2002;  69  FR 38855,

June 29, 2004]

##### § 141.74   Analytical and monitoring re- quirements.

  - Analytical requirements. Only the analytical method(s) specified in this paragraph, or otherwise approved by EPA, may be used to demonstrate com- pliance with §§ 141.71, 141.72 and 141.73. Measurements for  pH, turbidity,  tem- perature and residual disinfectant con- centrations must be conducted by a person approved by the State. Measure- ment for total coliforms, fecal coli- forms and HPC must be conducted by a laboratory certified by the State or EPA to do such analysis. Until labora- tory certification criteria are devel- oped for the analysis of fecal coliforms and HPC, any laboratory certified for total coliforms analysis by the State or EPA is deemed certified for fecal coli- forms and HPC analysis. The following procedures shall be conducted in ac- cordance with the publications  listed in the following section. This incorpo- ration by reference  was approved  by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies of the methods published in  Standard Methods for the Examination of Water and Wastewater may be obtained from the American Public Health Association et al., 1015 Fifteenth Street, NW., Washington, DC 20005; copies of the Minimal Medium ONPG-MUG Method as set forth in the article ‘‘National Field Evaluation of a Defined Substrate Method for the Si- multaneous Enumeration of Total Coli- forms and Esherichia coli from Drinking Water: Comparison with the Standard Multiple Tube Fermentation Method’’ (Edberg et al.), Applied and Environ- mental Microbiology, Volume 54, pp. 1595–1601, June 1988 (as amended under Erratum, Applied and Environmental Microbiology, Volume 54, p. 3197, De- cember, 1988),  may be obtained from

#### 40 CFR Ch. I (7–1–17 Edition)

the American Water Works Association Research Foundation, 6666 West Quincy Avenue, Denver, Colorado, 80235; and copies of the Indigo Method as set forth in the article ‘‘Determination of Ozone in Water by the Indigo Method’’ (Bader and  Hoigne),  may  be  obtained  from Ozone	Science	&	Engineering, Pergamon  Press  Ltd.,  Fairview  Park, Elmsford, New York 10523. Copies may be inspected at the U.S. Environmental Protection Agency, Room EB15, 401 M St.,  SW.,  Washington,  DC  20460  or  at the National Archives and Records Ad- ministration (NARA). For information on  the  availability  of  this  material  at NARA, call 202–741–6030.

| Organism | Methodology | Citation 1 |
| --- | --- | --- |
| Total Coliform 2 ..... Fecal Coliforms 2 ... Heterotrophic bac- teria 2. Turbidity 13 ............. | Total Coliform Fer- mentation Tech- nique 3 4 5. Total Coliform Membrane Filter Technique 6. ONPG-MUG Test 7 Fecal Coliform Procedure 8. Fecal Coliform Fil- ter Procedure. Pour Plate Method SimPlate 11. Nephelometric Method. Nephelometric Method. Great Lakes In- struments. | 9221 A, B, C 9222 A, B, C 9223 9221 E 9222 D 9215 B 2130 B 180.1 9 Method 2 10 |

Public water systems must con- duct analysis of pH and temperature in accordance with one of the methods listed at § 141.23(k)(1). Public water sys- tems must conduct analysis of total coliforms,	fecal	coliforms, heterotrophic   bacteria,   and   turbidity in accordance with one of the following analytical methods or one of the alter- native methods listed in appendix A to subpart C of this part and by using ana- lytical test procedures contained in Technical Notes on Drinking Water Meth- ods, EPA–600/R–94–173, October 1994. This document is available from the National Service Center for Environ- mental Publications (NSCEP), P.O. Box 42419, Cincinnati, OH 45242–0419 or .

#### Environmental Protection Agency	§ 141.74

| Organism | Methodology | Citation 1 |
| --- | --- | --- |
|  | Hach FilterTrak .... | 10133 12 |

The procedures shall be done in accordance with the docu- ments listed below. The incorporation by reference of the fol- lowing documents listed in footnotes 1, 6, 7 and 9–12 was ap- proved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies of the docu- ments may be obtained from the sources listed below. Infor- mation regarding obtaining these documents can be obtained from the Safe Drinking Water Hotline at 800–426–4791. Doc- uments may be inspected at EPA’s Drinking Water Docket, 1301  Constitution  Avenue,  NW.,  EPA  West,  Room  B102, Washington DC 20460 (Telephone: 202–566–2426); or at the National Archives and Records Administration (NARA). For in- formation  on  the  availability  of  this  material  at  NARA,  call 202–741–6030

1 Except where noted, all methods refer to Standard Meth- ods for the Examination of Water and Wastewater, 18th edi- tion (1992), 19th edition (1995), or 20th edition (1998), Amer- ican Public Health Association, 1015 Fifteenth Street, NW., Washington, DC 20005. The cited methods published in any of these three editions may be used. In addition, the following online versions may also be used: 2130 B–01, 9215 B–00, 9221 A, B, C, E–99, 9222 A, B, C, D–97, and 9223 B–97.

Standard     Methods     Online     are     The year in which each method was approved by the Standard Methods Committee is des- ignated  by  the  last  two  digits  in  the  method  number.  The methods listed are the only Online versions that may be used.

2 The time from sample collection to initiation of analysis may not exceed 8 hours. Systems must hold samples below 10 deg. C during transit.

3 Lactose broth, as commercially available, may be used in lieu of lauryl tryptose broth, if the system conducts at least 25 parallel tests between this medium and lauryl tryptose broth using the water normally tested, and this comparison dem- onstrates that the false-positive rate and false-negative rate for total coliform, using lactose broth, is less than 10 percent.

4 Media should cover inverted tubes at least one-half to two- thirds after the sample is added.

5 No requirement exists to run the completed phase on 10 percent of all total coliform-positive confirmed tubes.

6 MI agar also may be used. Preparation  and  use  of  MI agar is set forth in the article, ‘‘New medium for the simulta- neous detection of total coliform and Escherichia coli in water’’ by Brenner, K.P., et. al., 1993, Appl. Environ. Microbiol. 59:3534–3544. Also available from the Office of Water Re- source Center (RC–4100T), 1200 Pennsylvania Avenue, NW., Washington DC 20460, EPA/600/J–99/225. Verification of colonies is not required.

7 The ONPG-MUG Test is also known as the Autoanalysis Colilert System.

8 A–1 broth may be held up to 7 days in a tightly closed screw cap tube at 4 C.

9 ‘‘Methods for the Determination of Inorganic Substances in Environmental Samples’’, EPA/600/R–93/100, August 1993. Available at NTIS, PB94–121811.

10 GLI Method 2, ‘‘Turbidity,’’ November 2, 1992, Great Lakes Instruments, Inc., 8855 North 55th Street, Milwaukee, WI 53223.

11 A description of the SimPlate method, ‘‘IDEXX SimPlate TM HPC Test Method for Heterotrophs in Water,’’ November 2000, can be obtained from IDEXX Laboratories, Inc., 1 IDEXX Drive, Westbrook, ME 04092, telephone (800) 321–

0207.

12 A description of the Hach FilterTrak Method 10133, ‘‘De- termination of Turbidity by Laser Nephelometry,’’ January 2000, Revision 2.0, can be obtained from; Hach Co., P.O. Box 389, Loveland, CO 80539–0389, telephone: 800–227–

4224.

13 Styrene divinyl benzene beads (e.g., AMCO-AEPA–1 or equivalent) and stabilized formazin (e.g., Hach StablCal TM or equivalent) are acceptable substitutes for formazin.

- Public water systems must meas- ure residual disinfectant concentra- tions with one of the analytical meth- ods in the following table or one of the alternative methods listed in appendix A to subpart C of this part. If approved by the State, residual disinfectant con- centrations for free chlorine and com- bined chlorine also may be measured by using DPD colorimetric test kits. In addition States may approve the use of the ITS free chlorine test strip for the determination of free chlorine. Use of the test strips is described in Method D99–003, ‘‘Free Chlorine Species (HOCl¥ and OCl¥) by Test Strip,’’ Revision 3.0, November 21, 2003, available from In- dustrial Test Systems, Inc., 1875 Langston St., Rock Hill, SC 29730. Free and total chlorine residuals may be measured continuously by adapting a specified chlorine residual method for use with a continuous monitoring in- strument provided the chemistry, accu- racy, and precision remain the same. Instruments used for continuous moni- toring must be calibrated with a grab sample measurement at least every five days, or with a protocol approved by the State.

492

| Residual | Methodology | SM 1 | SM Online 2 | Other |
| --- | --- | --- | --- | --- |
| Free Chlorine .......................... | Amperometric Titration .......................................................... | 4500–Cl D ............................. | 4500–Cl D–00 ....................... | D1253–03 3 |
|  | DPD Ferrous Titrimetric ........................................................ | 4500–Cl F .............................. | 4500–Cl F–00. |  |
|  | DPD Colorimetric ................................................................... | 4500–Cl G ............................. | 4500–Cl G–00. |  |
|  | Syringaldazine (FACTS) ........................................................ | 4500–Cl H ............................. | 4500–Cl H–00. |  |
| Total Chlorine ......................... | Amperometric Titration .......................................................... | 4500–Cl D ............................. | 4500–Cl D–00 ....................... | D1253–03 3 |
|  | Amperometric Titration (low level measurement) ................. | 4500–Cl E .............................. | 4500–Cl E–00. |  |
|  | DPD Ferrous Titrimetric ........................................................ | 4500–Cl F .............................. | 4500–Cl F–00. |  |
|  | DPD Colorimetric ................................................................... | 4500–Cl G ............................. | 4500–Cl G–00. |  |
|  | Iodometric Electrode ............................................................. | 4500–Cl I ............................... | 4500–Cl I–00. |  |
| Chlorine Dioxide ..................... | Amperometric Titration .......................................................... | 4500–ClO2 C ......................... | 4500–ClO2 C–00. |  |
|  | DPD Method .......................................................................... | 4500–ClO2 D. |  |  |
|  | Amperometric Titration .......................................................... | 4500–ClO2 E ......................... | 4500–ClO2 E–00. |  |
|  | Spectrophotometric ............................................................... | ................................................ | ................................................ | 327.0, Revision 1.1 4 |
| Ozone ..................................... | Indigo Method ........................................................................ | 4500–O3 B ............................. | 4500–O3 B–97. |  |

§ 141.74

1 All the listed methods are contained in the 18th, 19th, and 20th editions of Standard Methods for the Examination of Water and Wastewater, 1992, 1995, and 1998; the cited methods published in any of these three editions may be used.

2 Standard Methods Online are available The year in which each method was approved by the Standard Methods Committee is designated by the last two digits in the method number. The methods listed are the only Online versions that may be used.

3 Annual Book of ASTM Standards, Vol. 11.01, 2004 ; ASTM International; any year containing the cited version of the method may be used. Copies of this method may be obtained from ASTM International, 100 Barr Harbor Drive, P.O. Box C700 West Conshohocken, PA 19428–2959.

40 CFR Ch. I (7–1–17 Edition)

4 EPA Method 327.0, Revision 1.1, ‘‘Determination of Chlorine Dioxide and Chlorite Ion in Drinking Water Using Lissamine Green B and Horseradish Peroxidase with Detection by Visible Spectrophotometry,’’ USEPA, May 2005, EPA 815–R–05–008.

#### Environmental Protection Agency	§ 141.74

  - Monitoring requirements for systems that do not provide filtration. A public water system that uses a surface water source and does not provide filtration treatment must begin monitoring, as specified in this paragraph (b), begin- ning December 31, 1990, unless  the State has determined that filtration is required     in     writing     pursuant     to

§ 1412(b)(7)(C)(iii), in which case the State may specify alternative moni- toring requirements, as appropriate, until filtration is in place.  A  public water system that uses a ground water source under the direct influence of surface water and does not provide fil- tration treatment must begin moni- toring as specified in this paragraph (b) beginning December 31, 1990, or 6 months after the State determines that the ground water source is under the direct influence of surface water, whichever is later, unless the State has determined that filtration is  required in	writing	pursuant	to

§ 1412(b)(7)(C)(iii), in which case the State may specify alternative moni- toring requirements, as appropriate, until  filtration  is  in  place.

    - Fecal coliform or total coliform density  measurements  as  required  by

§ 141.71(a)(1) must be performed on rep- resentative source water samples im- mediately prior to the  first  or  only point of  disinfectant application.  The system must sample for fecal or total coliforms at the following minimum frequency each week the system serves water to the public:

| System size (persons served) | Samples/ week 1 |
| --- | --- |
| 500 ....................................................................... | 1 |
| 501 to 3,300 .......................................................... | 2 |
| 3,301 to 10,000 ..................................................... | 3 |
| 10,001 to 25,000 ................................................... | 4 |
| >25,000 .................................................................. | 5 |

1 Must be taken on separate days.

Also, one fecal or total coliform den- sity measurement must be made every day the system serves water to  the public and the turbidity of the source water exceeds 1 NTU (these samples count towards the weekly coliform sampling requirement) unless the State determines that the system, for logistical  reasons  outside  the  system’s

control, cannot have the sample ana- lyzed within 30 hours of collection.

    - Turbidity measurements as re- quired by § 141.71(a)(2) must be per- formed on representative grab  samples of  source  water  immediately  prior  to the first or only point of disinfectant application every four hours (or more frequently) that the  system  serves water to the public. A public water sys- tem may substitute  continuous  tur- bidity monitoring for grab sample monitoring if it validates  the  contin- uous measurement for accuracy on a regular basis using a protocol  approved by  the  State.

    - The total inactivation ratio for each day that the system is in oper- ation must be determined based on the CT99.9  values in tables 1.1–1.6, 2.1, and

  - of this section, as appropriate. The parameters necessary to determine the total inactivation ratio must be mon- itored as follows:

    - The temperature of the disinfected water must be measured at least once per day at each residual disinfectant concentration sampling point.

    - If the system uses chlorine, the pH of the disinfected water must be measured at least once per day at each chlorine residual disinfectant con- centration sampling point.

    - The disinfectant contact time(s) (‘‘T’’) must be determined for each day during peak hourly flow.

    - The residual disinfectant con- centration(s) (‘‘C’’) of the water before or at the first customer must be meas- ured each day during peak hourly flow.

    - If a system uses a disinfectant other than chlorine, the system may demonstrate to the State, through the use of a State-approved protocol for on- site disinfection challenge studies or other information satisfactory to the State, that CT99.9 values other  than those specified in tables 2.1 and 3.1 in this section other operational param- eters are adequate to demonstrate that the system is achieving the minimum inactivation        rates        required        by

§ 141.72(a)(1).

#### § 141.74

| Resid- ual (mg/l) | pH |
| --- | --- |
|  | 6.0 | 6.5 | 7.0 | 7.5 | 8.0 | 8.5 | 9.0 |
| 0.4 ... | 137 | 163 | 195 | 237 | 277 | 329 | 390 |
| 0.6 ..... | 141 | 168 | 200 | 239 | 286 | 342 | 407 |
| 0.8 ..... | 145 | 172 | 205 | 246 | 295 | 354 | 422 |
| 1.0 ..... | 148 | 176 | 210 | 253 | 304 | 365 | 437 |
| 1.2 ..... | 152 | 180 | 215 | 259 | 313 | 376 | 451 |
| 1.4 ..... | 155 | 184 | 221 | 266 | 321 | 387 | 464 |
| 1.6 ..... | 157 | 189 | 226 | 273 | 329 | 397 | 477 |
| 1.8 ..... | 162 | 193 | 231 | 279 | 338 | 407 | 489 |
| 2.0 ..... | 165 | 197 | 236 | 286 | 346 | 417 | 500 |
| 2.2 ..... | 169 | 201 | 242 | 297 | 353 | 426 | 511 |
| 2.4 ..... | 172 | 205 | 247 | 298 | 361 | 435 | 522 |
| 2.6 ..... | 175 | 209 | 252 | 304 | 368 | 444 | 533 |
| 2.8 ..... | 178 | 213 | 257 | 310 | 375 | 452 | 543 |
| 3.0 ..... | 181 | 217 | 261 | 316 | 382 | 460 | 552 |

TABLE 1.1—CT VALUES (CT99.9) FOR 99.9 PER- CENT INACTIVATION OF GIARDIA  LAMBLIA CYSTS BY FREE CHLORINE AT 0.5 C OR LOWER 1

#### 40 CFR Ch. I (7–1–17 Edition)

TABLE 1.3—CT VALUES (CT 99.9) FOR 99.9 PERCENT  INACTIVATION  OF  GIARDIA  LAMBLIA CYSTS  BY  FREE  CHLORINE  AT  10.0  C 1—

Continued

| Free resid- ual (mg/l) | pH |
| --- | --- |
|  | 6.0 | 6.5 | 7.0 | 7.5 | 8.0 | 8.5 | 9.0 |
| 1.2 .. | 80 | 95 | 114 | 137 | 166 | 200 | 240 |
| 1.4 .. | 82 | 98 | 116 | 140 | 170 | 206 | 247 |
| 1.6 .. | 83 | 99 | 119 | 144 | 174 | 211 | 253 |
| 1.8 .. | 86 | 101 | 122 | 147 | 179 | 215 | 259 |
| 2.0 .. | 87 | 104 | 124 | 150 | 182 | 221 | 265 |
| 2.2 .. | 89 | 105 | 127 | 153 | 186 | 225 | 271 |
| 2.4 .. | 90 | 107 | 129 | 157 | 190 | 230 | 276 |
| 2.6 .. | 92 | 110 | 131 | 160 | 194 | 234 | 281 |
| 2.8 .. | 93 | 111 | 134 | 163 | 197 | 239 | 287 |
| 3.0 .. | 95 | 113 | 137 | 166 | 201 | 243 | 292 |

1 These CT values achieve greater than a 99.99 percent in- activation of viruses. CT values between the indicated pH val- ues may be determined by linear interpolation. CT values be- tween the indicated temperatures of different tables may be determined by linear interpolation. If no interpolation is used, use the CT99.9 value at the lower temperature and at the high- er pH.

TABLE 1.2—CT VALUES (CT 99.9) FOR 99.9

1 These CT values achieve greater than a 99.99 percent in- activation of viruses. CT values between the indicated pH val- ues may be determined by linear interpolation. CT values be- tween the indicated temperatures of different tables may be determined by linear interpolation. If no interpolation is used, use the CT99.9 value at the lower temperature, and at the higher pH.

TABLE 1.4—CT VALUES (CT 99.9) FOR 99.9 PERCENT  INACTIVATION  OF  GIARDIA  LAMBLIA

CYSTS BY FREE CHLORINE AT 15.0 C

1

| Free resid- ual (mg/l) | pH |
| --- | --- |
|  | 6.0 | 6.5 | 7.0 | 7.5 | 8.0 | 8.5 | 9.0 |
| 0.4 ... | 49 | 59 | 70 | 83 | 99 | 118 | 140 |
| 0.6 .. | 50 | 60 | 72 | 86 | 102 | 122 | 146 |
| 0.8 .. | 52 | 61 | 73 | 88 | 105 | 126 | 151 |
| 1.0 .. | 53 | 63 | 75 | 90 | 108 | 130 | 156 |
| 1.2 .. | 54 | 64 | 76 | 92 | 111 | 134 | 160 |
| 1.4 .. | 55 | 65 | 78 | 94 | 114 | 137 | 165 |
| 1.6 .. | 56 | 66 | 79 | 96 | 116 | 141 | 169 |
| 1.8 .. | 57 | 68 | 81 | 98 | 119 | 144 | 173 |
| 2.0 .. | 58 | 69 | 83 | 100 | 122 | 147 | 177 |
| 2.2 .. | 59 | 70 | 85 | 102 | 124 | 150 | 181 |
| 2.4 .. | 60 | 72 | 86 | 105 | 127 | 153 | 184 |
| 2.6 .. | 61 | 73 | 88 | 107 | 129 | 156 | 188 |
| 2.8 .. | 62 | 74 | 89 | 109 | 132 | 159 | 191 |
| 3.0 .. | 63 | 76 | 91 | 111 | 134 | 162 | 195 |
| Free resid- ual (mg/l) | pH |
|  | 6.0 | 6.5 | 7.0 | 7.5 | 8.0 | 8.5 | 9.0 |
| 0.4 ... | 97 | 117 | 139 | 166 | 198 | 236 | 279 |
| 0.6 .. | 100 | 120 | 143 | 171 | 204 | 244 | 291 |
| 0.8 .. | 103 | 122 | 146 | 175 | 210 | 252 | 301 |
| 1.0 .. | 105 | 125 | 149 | 179 | 216 | 260 | 312 |
| 1.2 .. | 107 | 127 | 152 | 183 | 221 | 267 | 320 |
| 1.4 .. | 109 | 130 | 155 | 187 | 227 | 274 | 329 |
| 1.6 .. | 111 | 132 | 158 | 192 | 232 | 281 | 337 |
| 1.8 .. | 114 | 135 | 162 | 196 | 238 | 287 | 345 |
| 2.0 .. | 116 | 138 | 165 | 200 | 243 | 294 | 353 |
| 2.2 .. | 118 | 140 | 169 | 204 | 248 | 300 | 361 |
| 2.4 .. | 120 | 143 | 172 | 209 | 253 | 306 | 368 |
| 2.6 .. | 122 | 146 | 175 | 213 | 258 | 312 | 375 |
| 2.8 .. | 124 | 148 | 178 | 217 | 263 | 318 | 382 |
| 3.0 .. | 126 | 151 | 182 | 221 | 268 | 324 | 389 |

PERCENT  INACTIVATION  OF  GIARDIA  LAMBLIA CYSTS BY FREE CHLORINE AT 5.0 C 1

1 These CT values achieve greater than a 99.99 percent in- activation of viruses. CT values between the indicated pH val- ues may be determined by linear interpolation. CT values be- tween the indicated temperatures of different tables may be determined by linear interpolation. If no interpolation is used, use the CT99.9 value at the lower temperature, and at  the higher pH.

TABLE 1.3—CT VALUES (CT 99.9) FOR 99.9

1 These CT values achieve greater than a 99.99 percent in- activation of viruses. CT values between the indicated pH val- ues may be determined by linear interpolation. CT values be- tween the indicated temperatures of different tables may be determined by linear interpolation. If no interpolation is used, use the CT99.9 value at the lower temperature, and at  the higher pH.

TABLE 1.5—CT VALUES (CT99.9) FOR 99.9 PER-

CENT    INACTIVATION    OF    GIARDIA    LAMBLIA CYSTS BY FREE CHLORINE AT 20 C

1

| Free resid- ual (mg/l) | pH |
| --- | --- |
|  | 6.0 | 6.5 | 7.0 | 7.5 | 8.0 | 8.5 | 9.0 |
| 0.4 ... | 36 | 44 | 52 | 62 | 74 | 89 | 105 |
| 0.6 ..... | 38 | 45 | 54 | 64 | 77 | 92 | 109 |
| 0.8 ..... | 39 | 46 | 55 | 66 | 79 | 95 | 113 |
| 1.0 ..... | 39 | 47 | 56 | 67 | 81 | 98 | 117 |
| 1.2 ..... | 40 | 48 | 57 | 69 | 83 | 100 | 120 |
| 1.4 ..... | 41 | 49 | 58 | 70 | 85 | 103 | 123 |
| 1.6 ..... | 42 | 50 | 59 | 72 | 87 | 105 | 126 |

PERCENT  INACTIVATION  OF  GIARDIA  LAMBLIA CYSTS BY FREE CHLORINE AT 10.0 C 1

| Free resid- ual (mg/l) | pH |
| --- | --- |
|  | 6.0 | 6.5 | 7.0 | 7.5 | 8.0 | 8.5 | 9.0 |
| 0.4 ... | 73 | 88 | 104 | 125 | 149 | 177 | 209 |
| 0.6 .. | 75 | 90 | 107 | 128 | 153 | 183 | 218 |
| 0.8 .. | 78 | 92 | 110 | 131 | 158 | 189 | 226 |
| 1.0 .. | 79 | 94 | 112 | 134 | 162 | 195 | 234 |

#### Environmental Protection Agency	§ 141.74

TABLE 1.5—CT VALUES (CT99.9) FOR 99.9 PER- CENT INACTIVATION OF GIARDIA  LAMBLIA CYSTS BY FREE CHLORINE AT 20 C 1—Con-

tinued

| Free resid- ual (mg/l) | pH |
| --- | --- |
|  | 6.0 | 6.5 | 7.0 | 7.5 | 8.0 | 8.5 | 9.0 |
| 0.4 ... | 24 | 29 | 35 | 42 | 50 | 59 | 70 |
| 0.6 ..... | 25 | 30 | 36 | 43 | 51 | 61 | 73 |
| 0.8 ..... | 26 | 31 | 37 | 44 | 53 | 63 | 75 |
| 1.0 ..... | 26 | 31 | 37 | 45 | 54 | 65 | 78 |
| 1.2 ..... | 27 | 32 | 38 | 46 | 55 | 67 | 80 |
| 1.4 ..... | 27 | 33 | 39 | 47 | 57 | 69 | 82 |
| 1.6 ..... | 28 | 33 | 40 | 48 | 58 | 70 | 84 |
| 1.8 ..... | 29 | 34 | 41 | 49 | 60 | 72 | 86 |
| 2.0 ..... | 29 | 35 | 41 | 50 | 61 | 74 | 88 |
| 2.2 ..... | 30 | 35 | 42 | 51 | 62 | 75 | 90 |
| 2.4 ..... | 30 | 36 | 43 | 52 | 63 | 77 | 92 |
| 2.6 ..... | 31 | 37 | 44 | 53 | 65 | 78 | 94 |
| 2.8 ..... | 31 | 37 | 45 | 54 | 66 | 80 | 96 |
| 3.0 ..... | 32 | 38 | 46 | 55 | 67 | 81 | 97 |

TABLE 1.6—CT VALUES (CT99.9) FOR 99.9 PER- CENT INACTIVATION OF GIARDIA  LAMBLIA CYSTS BY FREE CHLORINE AT 25 C 1 AND HIGHER

| Free resid- ual (mg/l) | pH |
| --- | --- |
|  | 6.0 | 6.5 | 7.0 | 7.5 | 8.0 | 8.5 | 9.0 |
| 1.8 ..... 2.0 ..... 2.2 ..... 2.4 ..... 2.6 ..... 2.8 ..... 3.0 ..... | 43 44 44 45 46 47 47 | 51 52 53 54 55 56 57 | 61 62 63 65 66 67 68 | 74 75 77 78 80 81 83 | 89 91 93 95 97 99 101 | 108 110 113 115 117 119 122 | 129 132 135 138 141 143 146 |

1 These CT values achieve greater than a 99.99 percent in- activation of viruses. CT values between the indicated pH val- ues may be determined by linear interpolation. CT values be- tween the indicated temperatures of different tables may be determined by linear interpolation. If no interpolation is used, use the CT99.9 value at the lower temperature, and at  the higher pH.

1 These CT values achieve greater than a 99.99 percent in- activation of viruses. CT values between the indicated pH val- ues may be determined by linear interpolation. CT values be- tween the indicated temperatures of different tables may be determined by linear interpolation. If no interpolation is used, use the CT99.9 value at the lower temperature, and at the higher pH.

TABLE 2.1—CT VALUES (CT99.9) FOR 99.9 PERCENT INACTIVATION OF GIARDIA LAMBLIA CYSTS BY

CHLORINE DIOXIDE AND OZONE 1

|  | Temperature |
| --- | --- |
|  | <1 C | 5 C | 10 C | 15 C | 20 C | 25 C |
| Chlorine dioxide ........................................................................ | 63 | 26 | 23 | 19 | 15 | 11 |
| Ozone ........................................................................................ | 2.9 | 1.9 | 1.4 | 0.95 | 0.72 | 0.48 |

1 These CT values achieve greater than 99.99 percent inactivation of viruses. CT values between the indicated temperatures may be determined by linear interpolation. If no interpolation is used, use the CT99.9 value at the lower temperature for deter- mining CT99.9 values between indicated temperatures.

TABLE 3.1—CT VALUES (CT 99.9) FOR 99.9 PERCENT  INACTIVATION  OF  GIARDIA  LAMBLIA CYSTS BY CHLORAMINES 1

Temperature

| <1 C | 5 C | 10 C | 15 C | 20 C | 25 C |
| --- | --- | --- | --- | --- | --- |
| 3,800 | 2,200 | 1,850 | 1,500 | 1,100 | 750 |

1 These values are for pH values of 6 to 9. These CT val- ues may be assumed to achieve greater than 99.99 percent inactivation of viruses only if chlorine is added and mixed in the water prior to the addition of ammonia. If this condition is not met, the system must demonstrate, based on on-site stud- ies or other information, as approved by the State, that the system is achieving at least 99.99 percent inactivation of vi- ruses. CT values between the indicated temperatures may be determined by linear interpolation. If no interpolation is used, use the CT99.9 value at the lower temperature for determining CT99.9 values between indicated temperatures.

    - The total inactivation ratio must be calculated as follows:

      - If the system uses only one point of disinfectant application, the system may  determine  the  total  inactivation

ratio  based  on  either  of  the  following two methods:

- One inactivation ratio (CTcalc/ CT99.9) is determined before or at the first customer during peak hourly flow and if the CTcalc/CT99.9 1.0, the 99.9 percent Giardia lamblia inactivation re- quirement has been achieved; or

- Successive CTcalc/CT99.9 values, representing sequential inactivation ratios, are determined between the point of disinfectant application and a point before or at the first customer during peak hourly flow. Under this al- ternative, the following method must be used to calculate the total inactiva- tion ratio:

#### § 141.74

(1)

40 CFR Ch. I (7–1–17 Edition)

Determine CTcalc for each sequence.

CT99.9

## (2)	Add the  CTcalc  values together⎛(CTcalc)⎞

⎝

⎠

CT99.9

⎜	CT99.9  ⎟

## (3)

If	

## ⎛ CTcalc⎞

1.0, the 99.9 percent Giardia

## ⎜	⎟

⎝CT99.9 ⎠

lamblia inactivation requirement has been achieved.

      - If the system uses more than one point of disinfectant application before or at the first customer, the system must determine the CT value of each disinfection sequence  immediately prior to the next point of disinfectant application during peak hourly  flow. The CTcalc/CT99.9 value of each se- quence and

## CTcalc

CT



99.9

must be calculated using the method in paragraph (b)(4)(i)(B) of this section to determine if the system is in compli- ance with § 141.72(a).

      - Although not required, the total percent inactivation for a system with one or more points of residual dis- infectant concentration monitoring may be calculated by solving the fol- lowing equation:

## Percent inactivation = 100 100

10z

## ⎛CTcalc⎞

where z =3 

continuous monitoring on an ongoing basis at the frequencies prescribed below:

| System size by population | Samples/ day 1 |
| --- | --- |
| <500 ....................................................................... | 1 |
| 501 to 1,000 .......................................................... | 2 |
| 1,001 to 2,500 ....................................................... | 3 |
| 2,501 to 3,300 ....................................................... | 4 |

1 The day’s samples cannot be taken at the same time. The sampling intervals are subject to State review and approval.

If at any time the residual disinfectant concentration falls below 0.2 mg/l in a system using grab sampling in lieu of continuous  monitoring,  the  system must take a grab sample every 4 hours until  the  residual   concentration   is equal to or greater than 0.2 mg/l.

(6)(i) Until March 31, 2016, the resid- ual disinfectant concentration must be measured at least at the same points in the distribution system and at  the same time as total coliforms are sam- pled, as specified in § 141.21. Beginning April 1, 2016, the residual disinfectant concentration must be measured at least at the same points in the dis- tribution system and at the same time as total coliforms are sampled, as spec-

⎜	⎟

⎝CT99.9 ⎠

    - The residual disinfectant con- centration of the water entering the distribution system must be monitored continuously, and  the  lowest  value must be recorded  each  day,  except  that if there is a failure in the continuous monitoring equipment, grab sampling every 4 hours may be conducted in lieu of continuous monitoring, but for  no more  than  5  working  days  following the failure of the equipment, and sys- tems serving 3,300 or fewer persons may take  grab  samples  in  lieu  of  providing

ified  in  §§ 141.854  through  141.858.  The

State may allow a public water system which uses both a surface water source or a ground water source under direct influence of surface water,  and  a ground water source, to take disinfect- ant residual samples at points other than  the  total  coliform   sampling points if the State  determines  that such points are more representative of treated (disinfected) water quality within the distribution system. Heterotrophic bacteria, measured as heterotrophic   plate   count   (HPC)   as

#### Environmental Protection Agency	§ 141.74

specified in paragraph (a)(1) of this sec- tion, may be measured in lieu of resid- ual disinfectant concentration.

(ii) If the State determines, based on site-specific considerations, that a sys- tem has no means for having a sample transported and analyzed for HPC by a certified laboratory under the requisite time and temperature conditions speci- fied by paragraph (a)(1) of this section and that the system is providing ade- quate disinfection in the distribution system, the requirements of paragraph (b)(6)(i) of this section do not apply to that system.

  - Monitoring requirements for systems using filtration treatment. A public water system that uses  a  surface  water source or a ground water source under the influence of surface water and pro- vides filtration treatment  must  mon- itor  in  accordance  with  this  paragraph

- beginning June 29, 1993, or when fil- tration  is  installed,  whichever  is  later.

  - Turbidity measurements as re- quired by § 141.73 must be performed on representative samples of the system’s filtered water every four hours  (or more frequently) that the system serves water to the public. A public water system may substitute contin- uous turbidity monitoring for grab sample monitoring if it validates the continuous measurement for accuracy on a regular basis using a protocol ap- proved by the State. For any systems using slow sand filtration or filtration treatment other than conventional treatment, direct filtration, or diato- maceous  earth  filtration,  the   State may reduce the sampling frequency to once per day if it determines that less frequent monitoring is sufficient to in- dicate effective filtration performance. For systems serving 500 or fewer per- sons, the State may reduce the  tur- bidity sampling frequency to once per day, regardless of the type of filtration treatment used, if the State deter- mines that less frequent monitoring is sufficient to indicate effective  filtra- tion performance.

  - The residual disinfectant con- centration of the water entering the distribution system must be monitored continuously, and the lowest value must be recorded each day, except that if there is a failure in the continuous monitoring equipment, grab sampling

every 4 hours may be conducted in lieu of continuous monitoring, but for  no more  than  5  working  days  following the failure of the equipment, and sys- tems serving 3,300 or fewer persons may take grab samples in lieu of providing continuous monitoring on an ongoing basis at the frequencies each day pre- scribed below:

| System size by population | Samples/ day 1 |
| --- | --- |
| 500 ....................................................................... | 1 |
| 501 to 1,000 .......................................................... | 2 |
| 1,001 to 2,500 ....................................................... | 3 |
| 2,501 to 3,300 ....................................................... | 4 |

1 The day’s samples cannot be taken at the same time. The sampling intervals are subject to State review and approval.

If at any time the residual disinfectant concentration falls below 0.2 mg/l in a system using grab sampling in lieu of continuous monitoring, the system must take a grab sample every 4 hours until the residual disinfectant con- centration  is  equal  to  or  greater  than

0.2 mg/l.

(3)(i) Until March 31, 2016, the resid- ual disinfectant concentration must be measured at least at the same  points  in the  distribution  system  and  at   the same time as total coliforms are sam- pled, as specified in § 141.21. Beginning April 1, 2016, the residual disinfectant concentration  must  be  measured  at least at the same points in the dis- tribution system and at  the  same  time as total coliforms are sampled, as spec- ified in §§ 141.854 through 141.858. The State may allow a public water system which uses both a  surface  water  source or a ground water source under direct influence of  surface  water,   and   a ground water source, to take disinfect- ant residual samples at  points  other than   the   total   coliform    sampling points  if  the  State   determines   that such points are more representative of treated  (disinfected)  water  quality within the distribution system. Heterotrophic bacteria, measured as heterotrophic plate count (HPC) as specified in paragraph (a)(1) of this sec- tion, may be measured in lieu  of  resid- ual   disinfectant   concentration.

- If the State determines, based on site-specific considerations, that a sys- tem has no means for having a sample transported and analyzed for HPC by a certified laboratory under the requisite

#### § 141.75

time and temperature conditions speci- fied by paragraph (a)(1) of this section and that the system is providing ade- quate disinfection in the distribution system, the requirements of paragraph (c)(3)(i) of this section do not apply to that  system.

[54 FR 27527, June 29, 1989, as amended at 59

FR  62470,  Dec.  5,  1994;  60  FR  34086,  June  29,

1995;  64  FR  67465,  Dec.  1,  1999;  67  FR  65252,

Oct. 23, 2002; 67 FR 65901, Oct. 29, 2002; 69 FR

38856, June 29, 2004; 72 FR 11247, Mar. 12, 2007;

74  FR 30958,  June 29,  2009;  78  FR 10347,  Feb.

13, 2013]

##### § 141.75   Reporting  and  recordkeeping requirements.

  - A public water system that uses a surface water source and does not pro- vide filtration  treatment  must  report monthly to the State the information specified in this paragraph (a) begin- ning December 31, 1990, unless  the State has determined that filtration is required in writing pursuant to section 1412(b)(7)(C)(iii), in which case the State may  specify  alternative  report- ing requirements, as appropriate, until filtration is in place. A public water system that uses a ground water source under the direct influence of surface water and does not provide filtration treatment must report monthly to the State the information specified in this paragraph (a) beginning December 31, 1990, or 6 months after the State deter- mines that the ground water source is under the direct influence of surface water, whichever is later, unless the State has determined that filtration is required     in     writing     pursuant     to

§ 1412(b)(7)(C)(iii), in which case the State may  specify  alternative  report- ing requirements, as appropriate, until filtration  is  in  place.

    - Source water quality information must be reported to the State within 10 days after the end of each month the system serves water to the public. In- formation that must be reported in- cludes:

      - The cumulative number of months for which results are reported.

      - The number of fecal and/or total coliform samples, whichever are ana- lyzed during the month (if a system monitors for both, only fecal coliforms must be reported), the dates of sample

#### 40 CFR Ch. I (7–1–17 Edition)

collection, and the dates when the tur- bidity level exceeded 1 NTU.

      - The number of samples during the month that had equal to or less than 20/100 ml fecal coliforms and/or equal to or less than 100/100 ml total coliforms, whichever are analyzed.

      - The cumulative number of fecal or total coliform samples, whichever are analyzed, during the previous six months the system served water to the public.

      - The cumulative number of sam- ples that had equal to or less than 20/

100 ml fecal coliforms or equal to or less than 100/100 ml total coliforms, whichever are analyzed, during the pre- vious six months the system served water to the public.

      - The percentage of samples that had equal to or less than 20/100 ml fecal coliforms or equal to or less than 100/

100 ml total coliforms, whichever are analyzed, during the previous six months the system served water to the public.

      - The maximum turbidity level measured during the month, the date(s) of occurrence for any measurement(s) which exceeded 5 NTU, and the date(s) the occurrence(s) was reported to the State.

      - For the first 12 months of rec- ordkeeping, the dates and cumulative number of events during which the tur- bidity exceeded 5 NTU, and after one year of recordkeeping for turbidity measurements, the dates and cumu- lative number of events during which the turbidity exceeded 5 NTU in the previous 12 months the system served water to the public.

      - For the  first 120  months  of rec- ordkeeping, the dates and cumulative number of events during which the tur- bidity exceeded 5 NTU, and after 10 years of recordkeeping for turbidity measurements, the dates and cumu- lative number of events during which the turbidity exceeded 5 NTU in the previous 120 months the system served water to the public.

    - Disinfection information specified in § 141.74(b) must be reported to the State within 10 days after the end of each month the system serves water to the public. Information that must be reported includes:

#### Environmental Protection Agency	§ 141.75

      - For each day, the lowest measure- ment of residual disinfectant con- centration in mg/l in water entering the distribution system.

      - The date and duration of each pe-

where:

## V c d e 100 a b

riod when the residual disinfectant concentration in water entering the distribution system fell below 0.2 mg/l and when the State was notified of the occurrence.

      - The daily residual disinfectant concentration(s) (in mg/l) and dis- infectant contact time(s) (in minutes) used for calculating the CT value(s).

      - If chlorine is used, the daily measurement(s) of pH of disinfected water following each point of chlorine disinfection.

      - The daily measurement(s) of water temperature in C following each point of disinfection.

      - The daily CTcalc and CTcalc/ CT99.9 values for each disinfectant measurement or sequence and the sum of all CTcalc/CT99.9 values ((CTcalc/ CT99.9)) before or at the first customer.

      - The daily determination of whether disinfection achieves adequate Giardia cyst and virus inactivation, i.e., whether (CTcalc/CT99.9) is at least 1.0 or, where disinfectants other than chlorine are used, other indicator con- ditions that the State determines are appropriate, are met.

      - The following information  on the samples taken in the distribution system in conjunction with  total  coli- form monitoring pursuant to § 141.72:

- Number of instances where the residual disinfectant concentration is measured;

- Number of instances where the residual disinfectant concentration is not measured but heterotrophic bac- teria plate count (HPC) is measured;

- Number of instances where the re- sidual disinfectant concentration is measured but not detected and no HPC is measured;

- Number of instances where the residual disinfectant concentration is detected and where HPC is >500/ml;

- Number of instances where the residual disinfectant concentration is not measured and HPC is >500/ml;

- For the current and previous month the system served water to the public, the value of ‘‘V’’ in the fol- lowing formula:

a =  the value  in paragraph  (a)(2)(viii)(A) of

this section,

b = the value in paragraph (a)(2)(viii)(B) of this  section,

c = the value in paragraph (a)(2)(viii)(C) of this section,

d = the value in paragraph (a)(2)(viii)(D) of this section, and

e  =  the  value  in  paragraph  (a)(2)(viii)(E)  of this  section.

- If the State determines, based on site-specific considerations, that a sys- tem has no means for having a sample transported and analyzed for HPC by a certified laboratory under the requisite time and temperature conditions speci- fied by § 141.74(a)(1) and that the sys- tem is providing adequate  disinfection in the distribution system, the require- ments of paragraph (a)(2)(viii) (A)–(F) of this section do not apply to that sys- tem.

      - A system need not report the data listed in paragraphs (a)(2) (i), and (iii)–(vi) of this section if all data listed in paragraphs (a)(2) (i)–(viii) of this sec- tion remain on file at the  system,  and the  State  determines  that:

- The system has submitted to the State all the information required by paragraphs (a)(2) (i)–(viii) of this sec- tion for at least 12 months; and

- The State has determined that the system is not required to provide filtration  treatment.

    - No later than ten days after the end of each Federal fiscal year (Sep- tember 30), each system  must  provide to the State a  report  which  summa- rizes its compliance with all watershed control program requirements  specified in § 141.71(b)(2).

    - No later than ten days after the end of each Federal fiscal year (Sep- tember 30), each system  must  provide to the State a report on the on-site in- spection conducted during that year pursuant to § 141.71(b)(3), unless the on- site inspection was conducted by the State. If the inspection was  conducted by the State, the State must provide a copy of its report to the public water system.

#### § 141.75

(5)(i) Each system, upon discovering that a waterborne disease outbreak po- tentially attributable to that water system has occurred, must report that occurrence to the State as soon as pos- sible, but no later than by the end of the next business day.

- If at any time the turbidity ex- ceeds 5 NTU, the system must consult with the primacy agency as soon as practical, but no later than 24 hours after the exceedance is known, in ac- cordance with the public  notification requirements under § 141.203(b)(3).

- If at any time the residual falls below 0.2 mg/l in the water entering the distribution system, the system must notify the State as soon as possible, but no later than by the end of the next business day. The system also must no- tify the State by the end of the next business day whether or not the resid- ual was restored to at least 0.2 mg/l within 4 hours.

  - A public water system that uses a surface water source or a ground water source under the direct influence of surface water and provides filtration treatment must report monthly to the State the information specified in this paragraph (b) beginning June 29, 1993, or when filtration is installed, which- ever is later.

    - Turbidity measurements as re- quired by § 141.74(c)(1) must be reported within 10 days after the end of each month the system serves water to the public. Information that must be re- ported includes:

- The total number of filtered water turbidity measurements taken  during the  month.

- The number and percentage of fil- tered water turbidity measurements taken during the month which are less than or equal to the turbidity limits specified in § 141.73 for the filtration technology being used.

- The date and value of any tur- bidity measurements taken during the month which exceed 5 NTU.

    - Disinfection information specified in § 141.74(c) must be reported to the State within 10 days after the end of each month the system serves water to the public. Information that must be reported includes:

      - For each day, the lowest measure- ment   of   residual   disinfectant   con-

#### 40 CFR Ch. I (7–1–17 Edition)

centration  in  mg/l  in  water  entering the distribution system.

      - The date and duration of each pe- riod when the residual disinfectant concentration in water entering the distribution system fell below 0.2 mg/l and when the State was notified of the occurrence.

      - The following information on the samples taken in the distribution sys- tem in conjunction with total coliform monitoring pursuant to § 141.72:

        - Number of instances where the residual disinfectant concentration is measured;

        - Number of instances where the residual disinfectant concentration is not measured but heterotrophic bac- teria plate count (HPC) is measured;

        - Number of instances where the re- sidual disinfectant concentration is measured but not detected and no HPC is measured;

        - Number of instances where no re- sidual disinfectant concentration is de- tected and where HPC is >500/ml;

        - Number of instances where the residual disinfectant concentration is not measured and HPC is >500/ml;

        - For the current and previous month the system serves water to the public, the value of ‘‘V’’ in the fol- lowing formula:

## V c d e 100 a b

where:

a = the value in paragraph (b)(2)(iii)(A) of this section,

b  =  the  value  in  paragraph  (b)(2)(iii)(B)  of this  section,

c  =  the  value  in  paragraph  (b)(2)(iii)(C)  of this  section,

d  =  the  value  in  paragraph  (b)(2)(iii)(D)  of this section, and

e  =  the  value  in  paragraph  (b)(2)(iii)(E)  of this  section.

        - If the State determines, based on site-specific considerations, that a sys- tem has no means for having a sample transported and analyzed for HPC by a certified laboratory within the req- uisite time and temperature conditions specified by § 141.74(a)(1) and that the system is providing adequate disinfec- tion in the distribution system, the re- quirements of paragraph (b)(2)(iii) (A)–

- of this section do not apply.

#### Environmental Protection Agency	§ 141.76

      - A system need not report the data listed in paragraph (b)(2)(i) of this section if all data listed in paragraphs (b)(2) (i)–(iii) of this section remain on file at the system and the State deter- mines that the system has  submitted all the information required by para- graphs (b)(2) (i)–(iii) of this section for at least 12 months.

(3)(i) Each system, upon discovering that a waterborne disease outbreak po- tentially attributable to that water system has occurred, must report that occurrence to the State as soon as pos- sible, but no later than by the end of the next business day.

- If at any time the turbidity ex- ceeds 5 NTU, the system must consult with the primacy agency as soon as practical, but no later than 24 hours after the exceedance is known, in ac- cordance with the public  notification requirements under § 141.203(b)(3).

- If at any time the residual falls below 0.2 mg/l in the water entering the distribution system, the system must notify the State as soon as possible, but no later than by the end of the next business day. The system also must no- tify the State by the end of the next business day whether or not the resid- ual was restored to at least 0.2 mg/l within 4 hours.

[54 FR 27527, June 29, 1989, as amended at 65

FR  26022,  May  4,  2000;  69  FR  38856,  June  29,

2004]

##### § 141.76   Recycle provisions.

- Applicability. All subpart H sys- tems that employ conventional filtra- tion or direct filtration treatment and that recycle spent filter backwash water, thickener supernatant, or liq- uids from dewatering processes must meet the requirements in paragraphs

- through (d) of this section.

  - Reporting. A system must notify the State in writing by Decemeber 8, 2003, if the system recycles spent filter backwash water, thickener super- natant, or liquids from dewatering processes. This notification must in- clude, at a minimum, the information specified in paragraphs (b)(1) and (2) of this  section.

    - A plant schematic showing the or- igin of all flows which are recycled (in- cluding, but not limited to, spent filter backwash    water,    thickener    super-

natant, and liquids from dewatering processes), the hydraulic conveyance used to transport them, and the loca- tion where they are re-introduced back into  the  treatment  plant.

    - Typical recycle flow in gallons per minute (gpm), the highest observed plant flow experienced in the previous year (gpm), design flow for the treat- ment plant (gpm), and State-approved operating capacity  for the plant  where the State has made such determina- tions.

  - Treatment technique requirement. Any system that recycles spent filter backwash water, thickener super- natant, or liquids from dewatering processes must return these flows through the processes of a system’s ex- isting conventional or direct filtration system as defined in § 141.2 or at an al- ternate location approved by the  State by June 8, 2004. If capital  improve- ments are required to modify the recy- cle location to meet this  requirement, all capital improvements must be com- pleted no later than June 8, 2006.

  - Recordkeeping. The system must collect and retain on file recycle flow information specified in paragraphs (d)(1) through (6) of this section for re- view and evaluation by the State be- ginning June 8, 2004.

    - Copy of the recycle notification and information submitted to the State under paragraph (b) of this sec- tion.

    - List of all recycle flows and the frequency with which they are re- turned.

    - Average and maximum backwash flow rate through the filters and the average and maximum duration of the filter backwash process in minutes.

    - Typical filter run length and a written summary of how filter run length is determined.

    - The type of treatment provided for the recycle flow.

    - Data on the physical dimensions of the equalization and/or treatment units, typical and maximum hydraulic loading rates, type of treatment chemi- cals used and average dose and fre- quency of use, and frequency at which solids are removed, if applicable.

[66 FR 31103, June 8, 2001]

#### § 141.80

Subpart I—Control of Lead and Copper

SOURCE:  56  FR  26548,  June  7,  1991,  unless

otherwise noted.

##### § 141.80   General requirements.

      - Applicability and effective dates. (1) The requirements of this subpart I con- stitute the national primary drinking water regulations for lead and copper. Unless otherwise indicated, each of the provisions of this subpart applies to community water systems and non- transient, non-community water sys- tems (hereinafter referred to as ‘‘water systems’’ or ‘‘systems’’).

(2)  [Reserved]

      - Scope. These regulations establish a treatment technique that includes re- quirements for corrosion control treat- ment, source water treatment, lead service line replacement, and public education. These requirements are triggered, in some cases, by lead and copper action levels measured in sam- ples collected at consumers’ taps.

      - Lead and copper action levels. (1) The lead action level is exceeded if the concentration of lead in more than 10 percent of tap water samples collected during any monitoring period con- ducted in accordance with § 141.86 is greater than 0.015 mg/L (i.e.,  if  the ‘‘90th percentile’’ lead level  is  greater than 0.015 mg/L).

- The copper action level is exceed- ed if the concentration of copper in more than 10 percent of tap water sam- ples collected during any monitoring period  conducted  in  accordance  with

§ 141.86 is greater than 1.3 mg/L (i.e., if the ‘‘90th percentile’’ copper level is greater than 1.3 mg/L).

- The 90th percentile lead and cop- per levels shall be computed as follows:

  - The results of all lead or copper samples taken during a monitoring pe- riod shall be placed in ascending order from the sample with the lowest con- centration to the sample with the high- est concentration. Each  sampling  re- sult shall be assigned a number, as- cending by single integers beginning with the number 1 for the sample with the lowest contaminant level. The number assigned to the sample with the  highest  contaminant  level  shall  be

#### 40 CFR Ch. I (7–1–17 Edition)

equal  to  the  total  number  of  samples taken.

  - The number of samples taken during the monitoring period shall be multiplied by 0.9.

  - The contaminant concentration in the numbered sample yielded by the calculation in paragraph (c)(3)(ii) is the 90th percentile contaminant level.

  - For water systems serving fewer than 100 people that collect 5 samples per monitoring period, the 90th per- centile is computed by taking the aver- age of the highest and second highest concentrations.

  - For a public water system that has been allowed by the State to  col- lect fewer than five samples in accord- ance with § 141.86(c), the sample result with the highest concentration is con- sidered the 90th percentile value.

      - Corrosion control treatment require- ments. (1) All water systems shall in- stall and operate optimal corrosion control  treatment  as  defined  in  § 141.2.

(2) Any water system that complies with the applicable corrosion control treatment  requirements  specified   by the State under §§ 141.81 and 141.82 shall be deemed in compliance with the treatment requirement contained in paragraph (d)(1) of this section.

      - Source water treatment require- ments.  Any  system  exceeding  the   lead or copper action level shall  implement all applicable source water treatment requirements specified by  the  State under § 141.83.

      - Lead service line replacement re- quirements. Any system exceeding the lead action level after implementation of applicable corrosion control and source water treatment requirements shall complete the lead service line re- placement  requirements  contained  in

§ 141.84.

      - Public education requirements. Pur- suant to § 141.85, all water  systems must provide a consumer notice of  lead tap water monitoring results  to  per- sons served at the sites (taps) that are tested. Any system exceeding the lead action level shall implement the public education    requirements.

      - Monitoring and analytical require- ments.  Tap  water  monitoring  for  lead

#### Environmental Protection Agency	§ 141.81

and copper, monitoring for water  qual- ity parameters, source water  moni- toring for  lead  and  copper,  and  anal- yses of  the  monitoring  results  under this subpart shall be completed in com- pliance with §§ 141.86, 141.87, 141.88, and

141.89.

      - Reporting requirements. Systems shall report to the State any informa- tion required by the treatment  provi- sions of this subpart and § 141.90.

      - Recordkeeping requirements. Sys- tems shall maintain records in accord- ance with § 141.91.

      - Violation of national primary drink- ing water regulations. Failure to comply with   the   applicable   requirements   of

§§ 141.80–141.91, including requirements established by the State pursuant to these provisions, shall constitute a vio- lation of the national primary drinking water regulations for lead and/or cop- per.

[56  FR  26548,  June  7,  1991;  57  FR  28788,  June

29,  1992,  as  amended  at  72  FR  57814,  Oct. 10,

2007]

##### § 141.81 Applicability of corrosion con- trol treatment steps to small, me- dium-size and large water systems.

- Systems shall complete the appli- cable corrosion control treatment re- quirements described in § 141.82 by  the deadlines  established  in  this  section.

  - A large system (serving >50,000 persons) shall complete the corrosion control treatment steps specified in paragraph (d) of this section, unless it is deemed to have optimized corrosion control under paragraph (b)(2) or (b)(3) of this section.

  - A small system (serving 3300 per- sons) and a medium-size system (serv- ing >3,300 and 50,000 persons) shall complete the corrosion control treat- ment steps specified in paragraph (e) of this section, unless  it  is  deemed  to have optimized corrosion control under paragraph (b)(1), (b)(2), or (b)(3) of this section.

- A system is deemed to have opti- mized corrosion control and is not re- quired to complete the applicable cor- rosion control treatment steps identi- fied in this section if the system satis- fies one of the criteria specified in paragraphs (b)(1) through (b)(3) of this section. Any such system deemed to have optimized corrosion control under

this paragraph, and which has treat- ment in place, shall continue to oper- ate and maintain optimal corrosion control treatment and meet any re- quirements that the State determines appropriate to ensure optimal corro- sion control treatment is maintained.

- A small or medium-size water sys- tem is deemed to have optimized corro- sion control  if  the  system  meets  the lead and copper action  levels  during each of two consecutive six-month monitoring periods conducted in ac- cordance with § 141.86.

- Any water system may be deemed by the State to have optimized corro- sion control treatment if the system demonstrates to the satisfaction of the State that it has conducted activities equivalent to the corrosion control steps applicable to such system under this section. If the State makes this determination, it shall provide the sys- tem with written notice explaining the basis for its decision and shall  specify the water quality control parameters representing optimal corrosion control in accordance with § 141.82(f). Water systems deemed to have optimized cor- rosion control under this paragraph shall operate in compliance with the State-designated optimal water quality control  parameters  in  accordance  with

§ 141.82(g) and continue to conduct lead and copper tap and water quality pa- rameter   sampling   in   accordance   with

§ 141.86(d)(3) and § 141.87(d), respectively. A system shall provide the State  with the following information in order to support a determination under this paragraph:

  - The results of all test samples col- lected for each of the water quality pa- rameters in § 141.82(c)(3).

  - A report explaining the test methods used by the water system to evaluate the corrosion control  treat- ments listed in § 141.82(c)(1), the results of all tests conducted, and the  basis  for the system’s selection of optimal cor- rosion   control   treatment;

  - A report explaining how corro- sion control has been installed and how it is being maintained to insure mini- mal lead and copper concentrations at consumers’ taps; and

  - The results of tap water samples collected in accordance with § 141.86 at least   once   every   six   months   for   one

#### § 141.81

year after corrosion control has been installed.

- Any water system is deemed to have optimized corrosion control if it submits results of tap water moni- toring   conducted   in   accordance   with

§ 141.86 and source water monitoring conducted in accordance with § 141.88 that demonstrates for two consecutive 6-month monitoring periods that the difference between the 90th percentile tap   water   lead   level   computed   under

§ 141.80(c)(3), and the highest source water  lead  concentration  is  less  than the  Practical  Quantitation  Level   for lead specified in § 141.89(a)(1)(ii).

  - Those systems whose highest source water lead level is below the Method Detection Limit may also be deemed to have optimized corrosion control under this paragraph if the 90th percentile tap water lead level is less than or equal to the Practical Quan- titation Level for lead for two consecu- tive 6-month monitoring periods.

  - Any water system deemed to have optimized corrosion control in accord- ance with this paragraph shall con- tinue monitoring for lead and copper at the tap no less frequently than once every three calendar years using the reduced  number  of  sites  specified  in

§ 141.86(c) and collecting the samples at times     and     locations     specified     in

§ 141.86(d)(4)(iv). Any such system that has not conducted a round of  moni- toring pursuant to § 141.86(d) since Sep- tember 30, 1997, shall complete a round of monitoring pursuant to this para- graph no later than September 30, 2000.

  - Any water system deemed to have optimized corrosion control pur- suant to this paragraph shall notify the    State    in    writing    pursuant    to

§ 141.90(a)(3) of any upcoming long-term change in treatment or addition of a new source as described in that section. The State must review and approve the addition of a new source or long-term change in water treatment before it is implemented by the water system. The State may require any such system to conduct additional monitoring or to take other action the State deems ap- propriate to ensure that such systems maintain minimal levels of  corrosion in the distribution system.

  - As of July 12, 2001, a system is not  deemed  to  have  optimized  corro-

#### 40 CFR Ch. I (7–1–17 Edition)

sion control under this paragraph, and shall implement corrosion control treatment pursuant to paragraph (b)(3)(v) of this section unless it meets the copper action level.

  - Any system triggered into corro- sion control because it is no longer deemed to have optimized corrosion control under this paragraph shall im- plement corrosion control treatment in accordance with the deadlines in para- graph (e) of this section. Any such large system shall adhere to the sched- ule specified in that paragraph for me- dium-size systems, with the time peri- ods for completing each step being triggered by the date the system is no longer deemed to have optimized corro- sion control under this paragraph.

- Any small or medium-size water system that is required to complete the corrosion control steps due to its ex- ceedance of the lead or copper action level may cease completing the  treat- ment steps whenever the system meets both action levels during each of two consecutive monitoring periods con- ducted pursuant to § 141.86 and submits the results to the  State.  If  any  such water  system  thereafter  exceeds   the lead or copper action level during any monitoring period, the system (or the State, as the case may be) shall recom- mence completion of the applicable treatment  steps,  beginning  with   the first treatment step which was not pre- viously completed in its entirety.  The State may require a system to repeat treatment steps  previously  completed by the system where the State deter- mines that this is necessary to imple- ment properly the treatment require- ments of this section. The  State  shall notify the system in writing of such a determination and explain the  basis  for its decision. The requirement for any small- or medium-size system to imple- ment corrosion control treatment  steps in accordance  with  paragraph  (e)  of this section (including systems  deemed to have optimized corrosion  control under paragraph (b)(1)  of  this  section) is triggered whenever any small- or medium-size  system  exceeds  the   lead or  copper  action  level.

- Treatment steps and deadlines for large systems. Except as provided in paragraph (b) (2) and (3) of this section,

#### Environmental Protection Agency	§ 141.82

large systems shall complete the fol- lowing  corrosion  control  treatment steps (described in the referenced por- tions of §§ 141.82, 141.86, and 141.87) by the  indicated  dates.

  - Step 1: The system shall conduct initial    monitoring    (§ 141.86(d)(1)    and

§ 141.87(b)) during two consecutive six- month  monitoring  periods   by   January 1, 1993.

  - Step 2: The  system  shall  complete corrosion control studies (§ 141.82(c)) by July 1, 1994.

  - Step 3: The State shall designate optimal    corrosion    control    treatment (§ 141.82(d)) by January 1, 1995.

  - Step 4: The system shall install op- timal     corrosion     control     treatment (§ 141.82(e)) by January 1, 1997.

  - Step 5: The system shall complete follow-up  sampling  (§ 141.86(d)(2)  and

§ 141.87(c)) by January 1, 1998.

  - Step 6: The State shall review in- stallation of treatment and designate optimal water quality control param- eters (§ 141.82(f)) by July 1, 1998.

  - Step 7: The system shall operate in compliance with the State-specified op- timal water quality control  parameters (§ 141.82(g)) and continue to conduct tap sampling (§ 141.86(d)(3) and § 141.87(d)).

- Treatment Steps and deadlines for small and medium-size systems. Except as provided in paragraph (b) of this sec- tion, small  and medium-size  systems shall complete the following corrosion control treatment steps (described in the   referenced   portions   of   §§ 141.82,

  - and 141.87) by the indicated time periods.

    - Step 1: The system shall conduct initial  tap  sampling  (§ 141.86(d)(1)  and

§ 141.87(b)) until the system either ex- ceeds the lead or copper action level or becomes eligible for reduced  moni- toring under § 141.86(d)(4). A system ex- ceeding the lead or copper action level shall recommend optimal corrosion control treatment  (§ 141.82(a))  within six months after the end of the moni- toring period during  which  it  exceeds one  of  the  action  levels.

    - Step 2: Within 12 months after the end of the monitoring period during which a system exceeds the lead or cop- per action level, the State may require the system to perform corrosion con- trol studies (§ 141.82(b)). If the State does not require the system to perform

such studies, the State shall specify op- timal    corrosion    control    treatment (§ 141.82(d)) within the following time- frames:

- For  medium-size  systems,  within

18 months after the end of the moni- toring period during which such system exceeds the lead or copper action level.

- For small systems, within 24 months after the end of the monitoring period during which such system ex- ceeds the lead or copper action level.

    - Step 3: If the State requires a sys- tem to perform corrosion control stud- ies under step 2, the system shall com- plete the studies (§ 141.82(c)) within 18 months after the State  requires  that such studies be conducted.

    - Step 4: If the system has per- formed corrosion control studies under step 2, the State shall designate opti- mal     corrosion     control     treatment (§ 141.82(d)) within 6 months after com- pletion of step 3.

    - Step 5: The system shall install op- timal    corrosion    control    treatment (§ 141.82(e)) within 24 months after the State  designates  such  treatment.

    - Step 6: The system shall complete follow-up  sampling  (§ 141.86(d)(2)  and

§ 141.87(c)) within 36 months after the State designates optimal corrosion control   treatment.

    - Step 7: The State shall review the system’s installation of treatment and designate optimal water  quality  con- trol parameters (§ 141.82(f)) within 6 months after completion of step 6.

    - Step 8: The system shall operate in compliance with the State-designated optimal water quality control param- eters (§ 141.82(g)) and continue to con- duct  tap  sampling  (§ 141.86(d)(3)  and

§ 141.87(d)).

[56 FR 26548, June 7, 1991, as amended at 59

FR 33862,  June 30,  1994;  65  FR 2004,  Jan. 12,

2000; 72 FR 57814, Oct. 10, 2007]

##### § 141.82   Description  of  corrosion  con- trol treatment requirements.

Each system shall complete the cor- rosion control treatment requirements described below which are applicable to such system under § 141.81.

- System recommendation regarding corrosion control treatment. Based upon the results of lead and copper tap mon- itoring and water quality parameter monitoring,    small    and    medium-size

#### § 141.82

water systems exceeding the lead or copper action level shall recommend installation of one or more of the cor- rosion control treatments listed in paragraph (c)(1) of this section which the system believes constitutes opti- mal corrosion control for that system. The State may require the system to conduct additional water quality pa- rameter monitoring in accordance with

§ 141.87(b) to assist the State in review- ing  the  system’s  recommendation.

- State decision to require studies of corrosion control treatment (applicable to small and medium-size systems). The State may require any small or me- dium-size system that exceeds the lead or copper action level to perform corro- sion  control  studies  under  paragraph

- of this section to identify optimal corrosion control treatment  for the system.

  - Performance of corrosion control studies. (1) Any public water system performing corrosion control studies shall evaluate the effectiveness of each of the following treatments, and, if ap- propriate, combinations of the fol- lowing treatments to identify the opti- mal corrosion control treatment for that system:

- Alkalinity and pH adjustment;

- Calcium hardness adjustment; and

- The addition of a phosphate or silicate based corrosion inhibitor at a concentration sufficient  to  maintain an effective residual concentration in all test tap samples.

      - The water system shall evaluate each of the corrosion control treat- ments using either pipe rig/loop tests, metal coupon tests, partial-system tests, or analyses based on documented analogous treatments with other sys- tems of similar size, water chemistry and distribution system configuration.

      - The water system shall measure the following water quality parameters in any tests conducted under this para- graph before and after evaluating the corrosion control treatments listed above:

        - Lead;

        - Copper;

        - pH;

        - Alkalinity;

        - Calcium;

        - Conductivity;

#### 40 CFR Ch. I (7–1–17 Edition)

        - Orthophosphate (when an inhib- itor containing a  phosphate  compound is used);

        - Silicate (when an inhibitor con- taining a silicate compound is used);

        - Water temperature.

      - The water system shall identify all chemical or physical  constraints that limit or prohibit the use of a par- ticular corrosion control treatment and document such constraints with at least one of the following:

        - Data and documentation showing that a particular corrosion control treatment has adversely affected other water treatment processes when used by another water system with com- parable water quality characteristics; and/or

        - Data and documentation dem- onstrating that  the  water  system has previously attempted to evaluate a particular corrosion control treatment and has found that the treatment is in- effective or adversely affects other water quality treatment processes.

      - The water system shall evaluate the effect of the chemicals used for cor- rosion control treatment on other water quality treatment processes.

      - On the basis of an analysis of the data generated during each evaluation, the water system shall recommend to the State in writing the treatment op- tion that the corrosion control studies indicate constitutes optimal corrosion control treatment for that system. The water system shall  provide a  rationale for its recommendation along with all supporting documentation specified in paragraphs (c) (1) through (5) of this section.

  - State designation of optimal corro- sion control treatment. (1) Based upon consideration of available information including, where applicable, studies performed under paragraph (c) of this section and a system’s recommended treatment alternative, the State shall either approve the corrosion control treatment option recommended by the system, or designate alternative corro- sion control treatment(s) from among those listed in paragraph (c)(1) of this section. When designating optimal treatment  the  State  shall  consider  the

#### Environmental Protection Agency	§ 141.82

effects that additional corrosion con- trol treatment will have on water qual- ity parameters and on other water quality  treatment  processes.

(2) The State shall notify the system of its decision on optimal corrosion control treatment in writing and ex- plain the basis for this determination. If the State requests additional infor- mation to aid its review, the water sys- tem shall provide the information.

  - Installation of optimal corrosion control. Each system shall properly in- stall and operate throughout its dis- tribution system the optimal corrosion control treatment designated by the State under paragraph (d) of this sec- tion.

  - State review of treatment and speci- fication of optimal water quality control parameters. The State shall evaluate the results of all lead and copper tap samples and water quality parameter samples submitted by the water system and determine whether the system has properly installed and operated the op- timal corrosion control treatment des- ignated by the State in paragraph (d) of this section. Upon reviewing the re- sults of tap water and water quality parameter monitoring by the system, both before and after the system in- stalls optimal corrosion control treat- ment, the State shall designate:

    - A minimum  value  or  a  range  of values for pH measured at each entry point to the distribution system;

    - A minimum pH value, measured in all tap samples. Such value shall be equal to or greater than 7.0, unless the State determines that meeting a pH level of 7.0 is not technologically fea- sible or is not necessary for the system to optimize corrosion control;

    - If a corrosion inhibitor is used, a minimum concentration or a range of concentrations for the inhibitor, meas- ured at each entry point to the dis- tribution system and in all tap sam- ples, that the State determines is nec- essary to form a passivating film  on the interior walls of the pipes of the distribution system;

    - If alkalinity is adjusted as part of optimal corrosion control treatment, a minimum concentration or a range of concentrations for alkalinity, meas- ured  at  each  entry  point  to  the  dis-

tribution system and in all tap sam- ples;

    - If calcium carbonate stabilization is used as part of corrosion control, a minimum concentration or a range of concentrations for calcium, measured in all tap samples.

The values for the applicable water quality control parameters  listed above shall be those that the State de- termines to reflect optimal corrosion control treatment for the system. The State may designate values for addi- tional water quality control param- eters determined by the State to re- flect optimal corrosion control for the system. The State shall notify the sys- tem in writing of these determinations and explain the basis for its decisions.

  - Continued operation and moni- toring. All systems optimizing corro- sion control shall continue to operate and maintain optimal corrosion con- trol treatment, including maintaining water quality parameters at or above minimum values or within ranges des- ignated by the State under paragraph

- of this  section,  in  accordance  with this paragraph for all samples collected under § 141.87(d) through  (f). Compli- ance with the requirements of this paragraph  shall  be  determined  every six       months,       as       specified       under

§ 141.87(d). A water system is out of compliance with the requirements of this paragraph for a six-month period if it has excursions for any State-speci- fied parameter on more than nine days during the period. An excursion occurs whenever the daily value for one or more of the water quality parameters measured at a sampling location is below the minimum value or outside the range designated by the  State. Daily values are calculated as follows. States have discretion to delete results of obvious sampling errors from this calculation.

  - On days when more than one measurement for the water quality pa- rameter is collected at the sampling lo- cation, the daily value shall be the av- erage of all results collected during the day regardless of whether they are col- lected through continuous monitoring, grab  sampling,  or  a  combination   of both. If EPA has approved an  alter- native formula under § 142.16 of this chapter  in  the  State’s  application  for  a

#### § 141.83

program   revision   submitted   pursuant to § 142.12 of this chapter, the State’s formula shall be used to aggregate multiple measurements taken at a sampling point for the water quality parameter in lieu of the formula in this paragraph.

  - On days when only one measure- ment for the  water  quality  parameter is collected at the sampling location, the daily value shall be the result of that  measurement.

  - On days when no measurement is collected for the water quality param- eter at the sampling location, the daily value shall be the daily value cal- culated on the most recent day  on which the water quality parameter was measured at the sample site.

- Modification of State treatment de- cisions. Upon its own initiative or in re- sponse to a request by a water system or other interested party, a State may modify its determination of the opti- mal corrosion control treatment under paragraph (d) of this section or optimal water quality control parameters under paragraph (f) of this section. A request for modification by a system or other interested party shall be in writ- ing, explain why the modification is appropriate, and provide supporting documentation. The State may modify its determination where it concludes that such change is necessary to ensure that the system continues to optimize corrosion control treatment. A revised determination shall  be  made in  writ- ing, set forth the new treatment re- quirements, explain the basis for the State’s decision, and provide an imple- mentation schedule for completing the treatment modifications.

- Treatment decisions by EPA in lieu of the State. Pursuant to the procedures in § 142.19, the EPA Regional Adminis- trator may review treatment deter- minations made by a State under para- graphs (d), (f), or (h) of this section and issue federal treatment determinations consistent with the requirements of those paragraphs where the Regional Administrator  finds  that:

  - A State has failed to issue a treat- ment determination by the applicable deadlines contained in § 141.81,

  - A State has abused its discretion in a substantial number of cases or in

#### 40 CFR Ch. I (7–1–17 Edition)

cases   affecting   a   substantial   popu- lation, or

  - The technical aspects of a State’s determination would be indefensible in an expected Federal enforcement ac- tion taken against a system.

[56 FR 26548, June 7, 1991, as amended at 65

FR 2004, Jan. 12, 2000]

##### § 141.83   Source   water   treatment   re- quirements.

Systems shall  complete  the  applica- ble source water monitoring and treat- ment requirements (described in the referenced portions of paragraph (b) of this section, and in §§ 141.86, and 141.88) by  the  following  deadlines.

- Deadlines for completing source water treatment steps—(1) Step 1: A sys- tem exceeding the lead or copper ac- tion level shall complete lead and cop- per        source         water        monitoring (§ 141.88(b)) and make a treatment rec- ommendation	to	the	State (§ 141.83(b)(1)) no later than 180 days after the end of the monitoring period during which the lead or copper action level  was  exceeded.

- Step 2: The State shall make a de- termination regarding source water treatment (§ 141.83(b)(2)) within 6 months after submission of monitoring results under step 1.

- Step 3: If the State requires instal- lation of source water treatment, the system   shall   install   the    treatment (§ 141.83(b)(3)) within 24 months after completion of step 2.

- Step 4: The system shall complete follow-up       tap       water       monitoring (§ 141.86(d)(2) and source water moni- toring (§ 141.88(c)) within 36 months after completion of step 2.

- Step 5: The State shall review the system’s installation and operation of source water treatment and specify maximum permissible source water levels (§ 141.83(b)(4)) within 6 months after completion of step 4.

- Step 6: The system shall operate in compliance with the State-specified maximum permissible lead and copper source water levels (§ 141.83(b)(4)) and continue    source    water    monitoring (§ 141.88(d)).

- Description of source water treat- ment requirements—(1) System treatment recommendation. Any system which ex- ceeds  the  lead  or  copper  action  level

#### Environmental Protection Agency	§ 141.83

shall recommend in writing to  the State the installation and operation of one of the source water treatments listed in paragraph (b)(2) of this sec- tion. A system may recommend  that no treatment be installed based upon a demonstration that source water treat- ment is not necessary to minimize lead and copper levels at users’ taps.

  - State determination regarding source water treatment. The State shall com- plete an evaluation of the results of all source water samples submitted by the water system to determine whether source water treatment is necessary to minimize lead or copper levels in water delivered to users’ taps. If the State de- termines that treatment is needed, the State shall either require installation and operation of the source water treatment recommended by the system (if any) or require the installation and operation of another source water treatment from among the following: Ion exchange, reverse osmosis, lime softening or coagulation/filtration. If the State requests additional informa- tion to aid in its review, the water sys- tem shall  provide  the  information by the date specified by the State in its request. The State shall notify the sys- tem in writing of its determination and set forth the basis for its decision.

  - Installation of source water treat- ment. Each system shall properly in- stall and operate the source water treatment designated by the State under paragraph (b)(2) of this section.

  - State review of source water treat- ment and specification of maximum per- missible source water levels. The State shall review the source water samples taken by the water system both before and after the system installs source water treatment, and determine wheth- er the system has properly installed and operated the source water treat- ment designated by the State. Based upon its review, the State shall des- ignate the maximum permissible lead and copper concentrations for finished water entering the distribution system. Such levels shall reflect the contami- nant removal capability of the treat- ment properly operated and main- tained. The State shall notify the sys- tem in writing and explain the basis for its decision.

  - Continued operation and mainte- nance. Each water  system  shall  main- tain lead and copper levels below the maximum permissible concentrations designated by the State  at  each  sam- pling  point  monitored  in  accordance with § 141.88. The system is out of com- pliance with this paragraph  if  the  level of lead or copper at any sampling point is greater than the  maximum  permis- sible concentration designated by the State.

  - Modification of State treatment deci- sions. Upon its own initiative or in re- sponse to a request by a water system or other interested party, a State may modify its determination of the source water treatment under paragraph (b)(2) of this section, or maximum permis- sible lead and copper concentrations for finished water entering the dis- tribution system under paragraph (b)(4) of this section. A request for modifica- tion by a system or other interested party shall be in writing, explain why the modification is appropriate, and provide supporting documentation. The State may modify its determination where it concludes that such change is necessary to ensure that the system continues to minimize lead and copper concentrations in source water. A re- vised determination shall be made in writing, set forth the new treatment requirements, explain the basis for the State’s decision, and provide an imple- mentation schedule for completing the treatment modifications.

  - Treatment decisions by EPA in lieu of the State. Pursuant to the procedures in § 142.19, the EPA Regional Adminis- trator may review treatment deter- minations made by a State under para- graphs (b) (2), (4), or (6) of this section and issue Federal treatment deter- minations consistent with the require- ments of those paragraphs where the Administrator  finds  that:

    - A State has failed to issue a treat- ment determination by the applicable deadlines contained in § 141.83(a),

    - A state has abused its discretion in a substantial number of cases or in cases affecting a substantial popu- lation, or

#### § 141.84

    - The technical aspects of a State’s determination would be inde- fensible in an expected Federal enforce- ment action taken against a system.

[56 FR 26548, June 7, 1991, as amended at 72

FR 57815, Oct. 10, 2007]

##### § 141.84   Lead service line replacement requirements.

(a) Systems that fail to meet the lead action level in tap samples taken pur- suant to § 141.86(d)(2), after installing corrosion control and/or source water treatment (whichever sampling occurs later), shall replace lead  service  lines in accordance with the requirements of this section. If a  system  is  in  violation of § 141.81 or § 141.83 for failure to install source water or corrosion control treatment, the State may require the system to commence lead service line replacement under this  section  after the date by which the system was re- quired   to   conduct   monitoring   under

§ 141.86(d)(2) has passed.

(b)(1) A water system shall replace annually at least 7 percent of  the  ini- tial number of lead service lines in its distribution system. The  initial  num- ber of lead service  lines  is  the  number of lead lines in place at the time the replacement program begins.  The  sys- tem shall identify the initial number of lead service lines in its distribution system, including  an  identification  of the portion(s) owned by the system, based on a materials evaluation, in- cluding   the   evaluation   required   under

§ 141.86(a) and relevant legal authorities (e.g., contracts, local ordinances) re- garding the portion owned by the sys- tem. The first year of lead service line replacement shall  begin  on  the  first day following the end of the  moni- toring period in which the action level was exceeded under paragraph (a) of this section. If monitoring is required annually or less frequently, the end  of the monitoring period is September 30 of the calendar year in which the sam- pling occurs. If the State has  estab- lished an alternate monitoring period, then the end of the monitoring period will be the last day of that period.

(2) Any water system resuming a lead service line replacement program after the cessation of its lead service line re- placement program as allowed by para- graph (f) of this section shall update its

#### 40 CFR Ch. I (7–1–17 Edition)

inventory of lead service lines to in- clude those sites that were previously determined not to require replacement through the sampling provision under paragraph (c) of this section. The sys- tem will then divide the updated num- ber of remaining lead service lines  by the number of remaining years in the program to determine the number of lines that must be replaced per year (7 percent lead service line replacement is based on a 15-year replacement pro- gram, so, for example, systems resum- ing lead service line replacement after previously conducting two years of re- placement would divide the updated in- ventory by 13). For those systems that have completed a 15-year lead service line replacement program,  the  State will determine a schedule for replacing or retesting lines that were previously tested out under the replacement pro- gram when the system re-exceeds the action  level.

- A system  is not required to re- place an individual lead service line  if the lead  concentration  in  all  service line samples from that line, taken pur- suant to § 141.86(b)(3), is less than or equal to 0.015 mg/L.

- A water system shall replace that portion of the lead service line that it owns. In cases where the system does not own the entire lead service  line, the system shall notify the owner  of the line, or the owner’s authorized agent, that the system will replace the portion of the service line that it owns and shall offer to replace the owner’s portion of the line. A system is not re- quired to bear the cost of replacing the privately-owned portion of the line, nor is it required to replace the privately- owned portion where the owner chooses not to pay the cost of replacing the pri- vately-owned portion of the line, or where replacing the privately-owned portion would be precluded by State, local or common law. A water system that does not replace the entire length of the service line also shall  complete the  following  tasks.

  - At least 45 days prior to com- mencing with the partial  replacement of a lead service line, the water system shall provide notice to  the  resident(s) of all buildings served by the line ex- plaining that they may experience a temporary   increase   of   lead   levels   in

#### Environmental Protection Agency	§ 141.85

their drinking water, along with guid- ance on measures consumers  can  take to minimize their exposure to lead. The State may allow the water system to provide notice under the previous sen- tence less than 45 days prior to com- mencing partial lead service line re- placement where such replacement  is in conjunction with emergency repairs. In addition,  the  water system  shall  in- form the resident(s) served by the line that the system will, at the system’s expense, collect a sample from each partially-replaced  lead   service   line that is representative of the water  in the service line for analysis of lead content,	as	prescribed	under

§ 141.86(b)(3), within 72 hours after the completion of the partial  replacement of the service line. The system shall collect the sample and report the re- sults of the analysis to the  owner  and the resident(s) served by the line with- in three business days of receiving the results. Mailed notices post-marked within three business days of receiving the results shall be considered ‘‘on time.’’

  - The water system shall provide the information required by paragraph (d)(1) of this section to the residents of individual dwellings by mail or by other methods approved by the State. In instances where multi-family dwell- ings are served by the line, the water system shall have the option to  post the information at a conspicuous loca- tion.

- The State shall require  a  system to replace lead service lines on a short- er schedule than that required by this section, taking into account the num- ber of lead service lines in the system, where such a shorter replacement schedule is feasible. The State shall make this determination  in  writing and notify the system of its finding within 6 months after the system is triggered into lead service line replace- ment based on monitoring  referenced in paragraph (a) of this section.

- Any system may cease replacing lead service lines whenever first draw samples       collected       pursuant       to

§ 141.86(b)(2) meet the lead action level during each of two consecutive moni- toring periods and the system submits the results to the State. If  first  draw tap  samples  collected  in  any  such  sys-

tem thereafter exceeds the lead action level, the system shall recommence re- placing lead service lines pursuant to paragraph (b)(2) of this section.

- To demonstrate compliance with paragraphs (a) through (d) of this sec- tion, a system shall report to the State the information specified in § 141.90(e).

[56  FR  26548,  June  7,  1991;  57  FR  28788,  June

29, 1992, as amended at 65 FR 2005, Jan. 12,

2000; 72 FR 57815, Oct. 10, 2007]

##### § 141.85   Public  education  and  supple- mental monitoring requirements.

All water systems must deliver a consumer notice of lead tap water mon- itoring results to persons served by the water system at sites  that  are  tested, as specified in paragraph (d) of this sec- tion. A water system that exceeds the lead action level based on tap water samples  collected  in  accordance  with

§ 141.86 shall deliver the public edu- cation materials contained  in  para- graph (a) of this section in accordance with the requirements in  paragraph  (b) of this section. Water systems that ex- ceed the lead action level must  sample the tap water of any customer who re- quests  it  in  accordance  with  paragraph

- of this section.

  - Content of written public education materials—(1) Community water systems and non-transient non-community water systems. Water systems must include the following elements in printed ma- terials (e.g., brochures and pamphlets) in the same order as listed below. In addition, language in paragraphs (a)(1)(i) through (ii) and (a)(1)(vi) of this section must be included in the materials, exactly as written, except for the text in brackets in these para- graphs for which the water system must include system-specific informa- tion. Any additional information pre- sented by a water system must be con- sistent with the information below and be in plain language that can be under- stood by the general public. Water sys- tems must submit all written public education materials to the State prior to delivery. The State may require the system to obtain approval of the con- tent of written public materials prior to delivery.

- IMPORTANT INFORMATION ABOUT LEAD IN YOUR DRINKING WATER. [INSERT NAME OF WATER

#### § 141.85

SYSTEM] found elevated levels of lead in drinking water in some homes/build- ings. Lead can cause serious health problems, especially for pregnant women and young children. Please read this information closely to see what you can do to reduce lead in your drinking water.

- Health effects of lead. Lead can cause serious health problems if too much enters your body from drinking water or other sources. It can cause damage to the brain and kidneys, and can interfere  with  the  production  of red blood cells that carry oxygen to all parts of your body. The greatest risk of lead exposure is to infants, young chil- dren, and pregnant women. Scientists have linked the effects of lead on the brain with lowered IQ in children. Adults with kidney problems and high blood pressure can be affected by low levels of lead  more  than  healthy adults. Lead is stored in the bones, and it can be released later in life. During pregnancy, the child receives lead from the mother’s bones, which may affect brain development.

- Sources of lead. (A) Explain what lead is.

  - Explain possible sources of lead in drinking water and how lead enters drinking water. Include information on home/building plumbing materials and service lines that may contain lead.

  - Discuss other important sources of lead exposure in addition to drinking water (e.g., paint).

- Discuss the steps the consumer can take to reduce their exposure to lead in drinking water.

  - Encourage running the water to flush out the lead.

  - Explain concerns with using hot water from the tap and specifically caution against the use of hot  water for preparing baby formula.

  - Explain that boiling water does not reduce lead levels.

  - Discuss other options consumers can take to reduce exposure to lead in drinking water, such as alternative sources or treatment of water.

  - Suggest that parents have their child’s blood tested for lead.

- Explain why there are elevated levels of lead in the system’s drinking water  (if  known)  and  what  the  water

#### 40 CFR Ch. I (7–1–17 Edition)

system is doing to reduce the lead lev- els in homes/buildings in this area.

- For more information, call us at [INSERT YOUR NUMBER] [(IF APPLI- CABLE), or visit our Web site at [IN- SERT YOUR WEB SITE HERE]]. For more information on reducing lead ex- posure around your home/building and the health effects of lead, visit EPA’s Web site or contact your health care provider.

- Community water systems. In addi- tion to including the elements speci- fied in paragraph (a)(1) of this section, community water systems must:

  - Tell consumers how to get their water tested.

  - Discuss lead in plumbing compo- nents and the difference between low lead and lead free.

  - Delivery of public education mate- rials. (1) For public water systems serv- ing a large proportion of non-English speaking consumers, as determined by the State, the public education mate- rials must contain information in the appropriate language(s) regarding the importance of the notice or contain a telephone number or address where persons served may contact the water system to obtain a translated copy of the public education materials or to re- quest assistance in the appropriate lan- guage.

- A community water system that exceeds the lead action  level  on  the basis of tap water samples collected in accordance with § 141.86, and that is not already conducting public education tasks under this section, must conduct the public education tasks under this section within 60 days after the  end  of the monitoring period in which the ex- ceedance  occurred:

  - Deliver printed materials meeting the content requirements of paragraph

- of this section to all bill paying cus- tomers.

(ii)(A) Contact customers who are most at risk by delivering education materials that meet the content re- quirements of paragraph (a) of this sec- tion to local public health agencies even if they are not located within the water system’s service area, along with an informational notice that encour- ages distribution to all the organiza- tion’s potentially affected customers or  community  water  system’s  users.

#### Environmental Protection Agency	§ 141.85

The water system must contact the local public health agencies directly by phone or in person. The local public health agencies may provide a specific list of additional community based or- ganizations serving target populations, which may include organizations out- side the service area of the water sys- tem. If such lists are provided, systems must deliver education materials that meet the content requirements of para- graph (a) of this section to all organi- zations on the provided lists.

- Contact customers who are  most at risk by delivering materials  that meet the content requirements of para- graph (a) of this section to the fol- lowing organizations listed in  1 through 6 that are located within the water system’s service area, along with an informational notice that encour- ages distribution to all the organiza- tion’s  potentially  affected  customers or community water system’s users:

  - Public and private schools or school boards.

  - Women, Infants and Children (WIC) and Head Start programs.

  - Public and private hospitals and medical clinics.

  - Pediatricians.

  - Family planning clinics.

  - Local welfare agencies.

- Make a good faith effort to locate the following organizations within the service area and deliver materials that meet the content requirements of para- graph (a) of this section to them, along with an informational notice that en- courages distribution to all potentially affected customers or users. The good faith effort to contact at-risk cus- tomers may include requesting a spe- cific contact list of these organizations from the local public health agencies, even if the agencies are not located within the water system’s service area:

  - Licensed childcare centers

  - Public and private preschools.

  - Obstetricians-Gynecologists and Midwives.

    - No less often than quarterly, provide information on or in each water bill as long as the system ex- ceeds the action level for lead. The message on the water bill must include the following statement exactly as written except for the text in brackets for  which  the  water  system  must  in-

clude system-specific information: [IN- SERT   NAME   OF   WATER   SYSTEM]

found high levels of lead in drinking water in some homes. Lead can cause serious health problems. For more in- formation please call [INSERT NAME OF WATER SYSTEM] [or visit (IN- SERT  YOUR  WEB  SITE  HERE)].  The

message or delivery mechanism can be modified in consultation with the State; specifically, the  State  may allow a separate mailing of public edu- cation materials to customers if the water system cannot place the infor- mation on water bills.

    - Post material meeting the con- tent requirements of paragraph (a) of this section on the water system’s Web site if the system serves a population greater than 100,000.

    - Submit a press release to news- paper, television and radio stations.

    - In addition to paragraphs (b)(2)(i) through (v) of this section, systems must implement at least three activi- ties from one or more categories listed below. The educational content and se- lection of these activities must be de- termined in consultation with the State.

      - Public Service Announcements.

      - Paid advertisements.

      - Public Area Information Dis- plays.

      - E-mails to customers.

      - Public Meetings.

      - Household Deliveries.

      - Targeted Individual Customer Contact.

      - Direct material distribution to all multi-family homes and institu- tions.

      - Other methods approved by the State.

    - For systems that are required to conduct monitoring annually or less frequently, the end of the monitoring period is September 30 of the calendar year in which  the  sampling  occurs,  or, if the State has established an alter- nate monitoring period, the last day of that  period.

- As long as a community water system exceeds the action level,  it must repeat the activities pursuant to paragraph (b)(2) of this section as de- scribed in paragraphs (b)(3)(i) through

- of this section.

#### § 141.85

  - A community water system shall repeat the tasks contained in para- graphs (b)(2)(i), (ii) and (vi) of this sec- tion every 12 months.

  - A community water system shall repeat tasks contained in paragraph (b)(2)(iii) of this section with each bill- ing cycle.

  - A community water system serv- ing a population greater than 100,000 shall post and retain material on a publicly  accessible  Web  site   pursuant to paragraph (b)(2)(iv) of this section.

  - The community water system shall repeat the task in paragraph (b)(2)(v) of this section twice every 12 months on a schedule agreed upon with the State. The State can allow activi- ties in paragraph (b)(2) of this section to extend beyond the 60-day require- ment if needed for implementation pur- poses on a case-by-case basis; however, this extension must be approved in writing by the State in advance of the 60-day deadline.

- Within 60 days after the end of the monitoring period in which the exceed- ance occurred (unless it already is re- peating public  education  tasks  pursu- ant to  paragraph  (b)(5)  of  this  section), a non-transient non-community water system shall deliver the public edu- cation materials specified  by  para- graph (a) of this section as follows:

  - Post informational posters on lead in drinking water in a public place or common area in each of the buildings served by the system; and

  - Distribute informational pam- phlets and/or brochures on lead in drinking water to each person served by the non-transient non-community water system. The State may allow the system to utilize electronic trans- mission in lieu of or combined with printed materials as long as it achieves at least the same coverage.

  - For systems that are required to conduct monitoring annually or less frequently, the end of the monitoring period is September 30 of the calendar year in which  the  sampling  occurs,  or, if the State has established an alter- nate monitoring period, the last day of that  period.

- A non-transient non-community water system shall repeat the tasks contained in paragraph (b)(4) of  this section at least once during each cal-

#### 40 CFR Ch. I (7–1–17 Edition)

endar year in which the system exceeds the lead action level. The State can allow activities in (b)(4) of this section to extend beyond the 60-day require- ment if needed for implementation pur- poses on a case-by-case basis; however, this extension must be approved in writing by the State in advance of the 60-day deadline.

- A water system may discontinue delivery  of   public   education   materials if the system has met the lead action level during the most recent six-month monitoring  period  conducted  pursuant to § 141.86. Such a system shall recom- mence public education in accordance with this section if it subsequently ex- ceeds the lead action level during any monitoring   period.

- A community water system may apply to the State, in writing  (unless the State has waived the requirement for prior State approval), to use  only the text specified in paragraph (a)(1) of this section in lieu of the text in para- graphs (a)(1) and (a)(2) of this section and to perform the tasks listed in para- graphs (b)(4) and (b)(5) of this section in lieu of the tasks in paragraphs (b)(2) and (b)(3) of this section if:

  - The system is a facility, such as a prison or a hospital, where the popu- lation served is not capable of or is pre- vented from making improvements to plumbing or installing point of use treatment devices; and

  - The system provides water  as part of the cost of services provided and does not separately charge for water consumption.

- A community water system serv- ing 3,300 or fewer people may limit cer- tain aspects of their public education programs as follows:

  - With respect to the  requirements of paragraph (b)(2)(vi) of this section, a system serving 3,300 or fewer must im- plement at least one of the activities listed in that paragraph.

  - With respect to the requirements of paragraph (b)(2)(ii) of this section, a system serving 3,300 or fewer people may limit the distribution of  the  pub- lic education materials required under that paragraph to facilities and organi- zations served by the system that are most likely to be visited regularly by pregnant women and children.

#### Environmental Protection Agency	§ 141.86

  - With respect to the requirements of paragraph (b)(2)(v) of this section, the State may waive this requirement for systems serving 3,300 or fewer per- sons as long as system distributes no- tices to every household served by the system.

  - Supplemental monitoring and notifi- cation of results. A water system that fails to meet the lead action  level  on the basis of tap samples collected in accordance with § 141.86 shall offer to sample the tap water of any customer who requests it. The system is not re- quired to pay for collecting or  ana- lyzing the sample, nor is the system re- quired to collect  and  analyze  the sam- ple  itself.

  - Notification of results—(1) Reporting requirement. All water systems must provide a notice of the individual tap results from lead tap water monitoring carried  out  under  the  requirements  of

§ 141.86 to the persons served by the water system  at  the  specific  sampling site from which the sample was taken (e.g., the occupants of the residence where the tap was tested).

- Timing of notification. A water sys- tem must provide the consumer notice as soon as practical, but no later than

30 days after the system learns of the tap  monitoring  results.

- Content. The consumer notice must include the results of lead tap water monitoring for the tap that was tested, an explanation of the health ef- fects of lead, list steps consumers can take to reduce exposure to lead in drinking water and contact informa- tion for the water utility. The notice must also provide the maximum con- taminant level goal and  the  action level for lead and the definitions for these two terms from § 141.153(c).

- Delivery. The consumer notice must be provided to persons served at the tap that was tested, either by mail or by another method approved by the State. For example, upon approval by the State, a non-transient non-commu- nity water system could post the re- sults on a bulletin board in the facility to allow users to review the informa- tion. The system must provide the no- tice to customers at sample taps test- ed, including consumers who do not re- ceive water bills.

[72 FR 57815, Oct. 10, 2007]

##### § 141.86   Monitoring   requirements   for lead and copper in tap water.

- Sample site location. (1) By the ap- plicable date for commencement of monitoring under paragraph (d)(1) of this section, each water system shall complete a materials evaluation of its distribution system in order to identify a pool of targeted sampling sites that meets the requirements of this section, and which is sufficiently large to en- sure that the water system can  collect the number of lead and copper tap sam- ples required in paragraph (c) of this section. All sites from which first draw samples are collected shall be selected from this pool of targeted  sampling sites. Sampling sites may not include faucets that have point-of-use or point- of-entry treatment  devices  designed to remove  inorganic  contaminants.

- A water system shall use the in- formation on lead, copper, and galva- nized steel that it is required to collect under § 141.42(d) of this part [special monitoring for corrosivity characteris- tics] when conducting a materials eval- uation. When an evaluation of the in- formation     collected     pursuant     to

§ 141.42(d) is insufficient to locate the requisite number of lead and copper sampling sites that meet the targeting criteria in paragraph (a) of this sec- tion, the water system shall review the sources of information listed below in order to identify a sufficient number of sampling sites. In addition, the system shall seek to collect such information where possible in the course of its nor- mal operations (e.g., checking service line materials when reading water me- ters or performing maintenance activi- ties):

  - All plumbing codes, permits, and records in the files of the building de- partment(s) which indicate the plumb- ing materials that are installed within publicly and privately owned struc- tures connected to the distribution sys- tem;

  - All inspections and records of the distribution system that indicate the material composition of the service connections that connect a  structure to the distribution system; and

  - All existing water quality infor- mation,  which  includes  the  results  of

#### § 141.86

all prior analyses of the system or indi- vidual structures connected to the sys- tem, indicating locations that may be particularly susceptible to high lead or copper  concentrations.

- The sampling sites selected for a community water system’s sampling pool (‘‘tier l sampling sites’’) shall con- sist of single family structures that:

  - Contain copper pipes with lead sol- der installed after 1982 or contain lead pipes; and/or

  - Are served by a lead service line. When multiple-family residences com- prise at least 20 percent of the struc- tures served by a water system, the system may include these types of structures in its sampling pool.

- Any community water  system with insufficient tier 1 sampling sites shall complete its sampling pool with ‘‘tier 2 sampling sites’’, consisting of buildings, including multiple-family residences that:

- Contain copper pipes with lead sol- der installed after 1982 or contain lead pipes; and/or

- Are served by a lead service line.

- Any  community  water   system with insufficient tier 1 and tier 2 sam- pling sites shall complete its sampling pool with ‘‘tier 3 sampling sites’’, con- sisting of single family structures that contain copper pipes with  lead solder installed before 1983.  A  community water system  with  insufficient  tier  1, tier 2, and tier 3 sampling sites shall complete its sampling pool with rep- resentative sites throughout the dis- tribution system.  For  the  purpose  of this paragraph,  a  representative  site  is a site in which the plumbing materials used at that site would be commonly found at  other sites served  by   the water   system.

- The sampling sites selected for a non-transient noncommunity water system (‘‘tier l sampling sites’’) shall consist of buildings that:

  - Contain copper pipes with lead sol- der installed after 1982 or contain lead pipes; and/or

  - Are served by a lead service line.

- A non-transient non-community water system with insufficient  tier  1 sites  that  meet   the   targeting   criteria in paragraph (a)(6) of this section shall complete its sampling pool with  sam- pling   sites   that   contain   copper   pipes

#### 40 CFR Ch. I (7–1–17 Edition)

with lead solder installed before 1983. If additional sites are needed to complete the sampling pool, the non-transient non-community water system shall use representative sites throughout the distribution system. For the purpose of this paragraph, a representative site is a site in which the plumbing materials used at that site would be commonly found at other sites served by the water system.

- Any water system whose distribu- tion system contains lead service lines shall draw 50 percent of the samples it collects during each monitoring period from sites that contain lead pipes, or copper pipes with lead solder, and 50 percent of the  samples  from  sites served by a lead service line. A water system that cannot identify a  suffi- cient number of sampling sites  served by a lead service line shall collect first- draw samples from all of the sites iden- tified as being served by such lines.

- Sample collection methods. (1) All tap samples for lead and copper  col- lected in accordance with this subpart, with the exception of lead service line samples collected under § 141.84(c) and samples collected under  paragraph (b)(5) of this section, shall be first-draw samples.

- Each first-draw tap sample  for lead and copper shall be one liter in volume and have stood motionless in the plumbing system of each sampling site for at least six hours. First-draw samples from residential housing shall be collected from the cold water kitch- en tap or bathroom  sink  tap.  First- draw samples from a nonresidential building shall be one liter in volume and shall be collected at an interior tap from which water is typically drawn for consumption. Non-first-draw sam- ples collected in lieu of first-draw sam- ples pursuant to paragraph (b)(5) of this section shall be one liter in vol- ume and shall be collected at an  inte- rior tap from which water is typically drawn for consumption. First-draw samples may be collected by the sys- tem or the system may allow residents to collect first-draw samples after in- structing the residents of the sampling procedures specified in this paragraph. To avoid problems of residents han- dling nitric acid, acidification of first- draw  samples  may  be  done  up  to  14

#### Environmental Protection Agency	§ 141.86

days after the sample is  collected. After acidification to resolubilize the metals, the sample must stand in the original container for the time speci- fied in the approved EPA method be- fore the sample can be analyzed. If a system allows residents to perform sampling, the system may not chal- lenge, based on alleged errors in sam- ple collection, the accuracy of sam- pling results.

- Each service line sample shall be one liter in volume and have stood mo- tionless in the lead service line for at least six hours. Lead service line sam- ples shall be collected in one of the fol- lowing three ways:

  - At the tap after flushing the vol- ume of water between the tap and the lead service line. The volume of water shall be calculated based on the inte- rior diameter and length of the pipe be- tween the tap and the lead service line;

  - Tapping directly into the lead service line; or

  - If the sampling site is a building constructed as a single-family resi- dence, allowing the water to run until there is a significant change in tem- perature which would be indicative of water that has been standing in the lead service line.

- A water system shall collect each first draw tap sample from the same sampling site from which it collected a previous sample. If, for any reason, the water system cannot gain entry to a sampling site in order to collect a fol- low-up tap sample, the system may col- lect the follow-up tap sample from an- other sampling site in  its  sampling pool as long as the new site meets the same targeting criteria, and is within reasonable proximity of the  original site.

- A non-transient non-community water system, or a community water system   that   meets   the   criteria   of

§ 141.85(b)(7), that does not have enough taps that can supply  first-draw  sam- ples, as defined in § 141.2, may apply to the State in writing to substitute non- first-draw samples. Such systems must collect as  many  first-draw  samples from appropriate taps as possible and identify sampling times and  locations that would likely result in the longest standing time  for  the  remaining  sites. The  State  has  the  discretion  to  waive

the requirement for prior State ap- proval of non-first-draw sample sites selected by the system, either through State regulation or written  notifica- tion to the system.

| System size (number of people served) | Number of sites (stand- ard moni- toring) | Number of sites (reduced moni- toring) |
| --- | --- | --- |
| >100,000 ................................................ | 100 | 50 |
| 10,001 to 100,000 ................................. | 60 | 30 |
| 3,301 to 10,000 ..................................... | 40 | 20 |
| 501 to 3,300 .......................................... | 20 | 10 |
| 101 to 500 ............................................. | 10 | 5 |

Number of samples. Water systems shall collect at least one sample during each monitoring period specified in paragraph (d) of this section from the number of sites listed in the first col- umn (‘‘standard monitoring’’) of the table in this paragraph. A system con- ducting reduced monitoring under paragraph (d)(4) of this section shall collect at least one sample from the number of sites specified in the second column (‘‘reduced monitoring’’) of the table in this paragraph during each monitoring period specified in para- graph (d)(4) of this section. Such re- duced monitoring sites shall be rep- resentative of the sites required for standard monitoring. A public water system that has fewer than five drink- ing water taps, that can be used for human consumption meeting the sam- ple site criteria of paragraph (a) of this section to reach the required number of sample sites listed in paragraph (c) of this section, must collect at least one sample from each tap and then must collect additional samples from those taps on different days during the moni- toring period to meet the required number of sites. Alternatively the State may allow these public water systems to collect a number of samples less than the number of sites specified in paragraph (c) of this section, pro- vided that 100 percent of all taps that can be used for human consumption are sampled. The State must approve this reduction of the minimum number of samples in writing based on a request from the system or onsite verification by the State. States may specify sam- pling locations when a system is con- ducting reduced monitoring. The table is as follows:

#### § 141.86

| System size (number of people served) | Number of sites (stand- ard moni- toring) | Number of sites (reduced moni- toring) |
| --- | --- | --- |
| 100 ....................................................... | 5 | 5 |

- Timing of monitoring—(1) Initial tap sampling. The first six-month moni- toring period for  small,  medium-size and large systems shall begin on the following dates:

| System size (No. people served) | First six-month moni- toring period begins on |
| --- | --- |
| >50,000 ......................................... 3,301 to 50,000 ............................. 3,300 ........................................... | January 1, 1992. July 1, 1992. July 1, 1993. |

- All large systems shall monitor during two consecutive six-month peri- ods.

- All small and medium-size sys- tems shall monitor during each six- month monitoring period until:

  - The system exceeds the lead or copper action level and is therefore re- quired to implement the corrosion con- trol    treatment    requirements    under

§ 141.81, in which  case the  system shall continue  monitoring  in   accordance with paragraph (d)(2) of this section, or

  - The system meets the lead and copper action levels during two con- secutive six-month monitoring periods, in which case the system may reduce monitoring in accordance with para- graph (d)(4) of this section.

- Monitoring after installation of cor- rosion control and source water treat- ment. (i) Any large system which in- stalls optimal corrosion control treat- ment pursuant to § 141.81(d)(4) shall monitor during two consecutive six- month monitoring periods by the date specified in § 141.81(d)(5).

- Any small or medium-size system which installs optimal corrosion con- trol treatment pursuant to § 141.81(e)(5) shall monitor during two consecutive six-month monitoring periods by the date specified in § 141.81(e)(6).

- Any system which installs source  water  treatment  pursuant  to

§ 141.83(a)(3) shall monitor during two consecutive six-month monitoring pe- riods     by     the     date     specified     in

§ 141.83(a)(4).

- Monitoring after State specifies water  quality  parameter  values  for  opti-

#### 40 CFR Ch. I (7–1–17 Edition)

mal corrosion control. After the State specifies the values for water quality control parameters under § 141.82(f), the system shall monitor during each sub- sequent six-month monitoring period, with the first monitoring period to begin on the date the State  specifies the optimal values under § 141.82(f).

- Reduced monitoring. (i) A small or medium-size water system that meets the lead and copper action levels dur- ing each of two consecutive six-month monitoring periods may reduce the number of samples in accordance with paragraph (c) of this section, and re- duce the frequency of sampling to once per year. A small or medium water sys- tem collecting fewer than five samples as specified in paragraph (c) of this sec- tion, that meets the lead and copper action levels during each of two con- secutive six-month monitoring periods may reduce the frequency of sampling to once per year. In no case can the system reduce the number of samples required below the minimum of one sample per available tap. This sam- pling shall begin during the calendar year immediately following the end of the second consecutive six-month mon- itoring period.

- Any water system that meets the lead action level and maintains the range of values for the water quality control parameters reflecting optimal corrosion control  treatment  specified by the State under § 141.82(f) during each of two consecutive six-month monitoring periods may reduce the fre- quency of monitoring to once per year and reduce the number of lead and cop- per samples in accordance with para- graph (c) of this section if it receives written approval from the State. This sampling shall begin during the cal- endar year immediately following the end of the second consecutive six- month monitoring period. The State shall  review  monitoring,  treatment, and other relevant information sub- mitted by the water system in accord- ance with § 141.90, and shall notify the system in writing when it determines the system is eligible to commence re- duced monitoring pursuant to this paragraph. The State shall review, and where appropriate, revise its deter- mination when the system submits new monitoring or treatment data, or when

#### Environmental Protection Agency	§ 141.86

other data relevant to the number and frequency of tap sampling becomes available.

- A small or medium-size water system that meets the lead and copper action levels during three consecutive years of monitoring may reduce the frequency of monitoring for  lead and copper from annually to once every three years. Any water system that meets the lead action level and main- tains the range of values for the water quality control parameters reflecting optimal corrosion control treatment specified by the State under § 141.82(f) during three consecutive years of mon- itoring may reduce the frequency of monitoring from annually to once every three years if it receives written approval from the State. Samples col- lected once every three years shall be collected no later than every third cal- endar year. The State shall review monitoring, treatment, and other rel- evant information submitted by the water    system    in    accordance    with

§ 141.90, and shall notify the system in writing when it determines the system is eligible  to reduce  the frequency  of monitoring to once every three years. The State shall review, and where ap- propriate, revise its determination when the system submits new moni- toring or treatment data, or when other data relevant to the number and frequency of tap sampling becomes available.

- A water system that reduces the number and frequency of sampling shall collect these samples from rep- resentative sites included in the pool of targeted sampling sites identified in paragraph (a) of this section. Systems sampling annually or less frequently shall conduct the lead and copper tap sampling during the months of June, July, August, or September unless the State has approved a different  sam- pling period in accordance with para- graph (d)(4)(iv)(A) of this section.

  - The State, at its discretion, may approve a different period for con- ducting the lead and copper tap sam- pling for systems collecting a reduced number of samples. Such a period shall be no longer than four consecutive months and must represent a time of normal operation where the highest levels of lead are most likely to occur.

For a non-transient non-community water system that does not operate during the months of June through September, and for which the period of normal operation where the highest levels of lead are most likely to occur is not known, the State shall designate a period that represents a time of nor- mal operation for the system. This sampling shall begin during the period approved or designated by the State in the calendar year immediately fol- lowing the end of the second consecu- tive six-month monitoring period for systems initiating annual monitoring and during the three-year period fol- lowing the end of the third consecutive calendar year of annual monitoring for systems initiating triennial moni- toring.

  - Systems monitoring  annually, that have been collecting samples dur- ing the months of June through Sep- tember and that receive State approval to alter their sample collection period under paragraph (d)(4)(iv)(A) of this section, must collect their  next  round of samples during a time period that ends no later than 21 months after the previous round of sampling. Systems monitoring triennially that have been collecting samples during the  months of June through September, and  re- ceive State approval to alter the sam- pling collection period as per para- graph (d)(4)(iv)(A) of this section, must collect their next round of samples dur- ing a time period that ends no later than 45 months after the previous round of sampling. Subsequent  rounds of sampling must be collected annually or triennially, as required by this sec- tion. Small systems with waivers, granted pursuant to paragraph (g) of this section, that have been collecting samples during the months of June through September and receive State approval to alter their sample collec- tion	period	under	paragraph (d)(4)(iv)(A) of this section must collect their next round of samples before the end of the 9-year period.

- Any water system that dem- onstrates for two consecutive 6-month monitoring periods that the tap water lead level computed under § 141.80(c)(3) is less than or equal to 0.005 mg/L and the tap water copper level computed under § 141.80(c)(3) is less than or equal

#### § 141.86

to 0.65 mg/L may reduce the number of samples  in  accordance  with  paragraph

- of this section and reduce the fre- quency of sampling to once every three calendar years.

(vi)(A) A small or medium-size water system subject to reduced monitoring that exceeds the lead or copper action level shall resume sampling in accord- ance with paragraph (d)(3) of this sec- tion and collect the number of samples specified for standard  monitoring under paragraph (c) of  this  section. Such a system shall also conduct water quality parameter monitoring in ac- cordance with § 141.87(b), (c) or (d) (as appropriate) during the monitoring pe- riod in which it exceeded the action level. Any such system may resume an- nual monitoring for lead and copper at the tap at the reduced number of sites specified in paragraph (c) of this sec- tion after it has completed two subse- quent consecutive six-month rounds of monitoring that meet the criteria of paragraph (d)(4)(i) of this section and/ or may  resume  triennial  monitoring for lead and copper at the reduced number of sites after it demonstrates through subsequent rounds of moni- toring that it meets the criteria of ei- ther paragraph (d)(4)(iii) or (d)(4)(v) of this  section.

(B) Any water system subject to the reduced monitoring frequency that fails to meet the lead action level dur- ing any four-month monitoring period or that fails to operate at or above the minimum value or within the range of values for the water quality param- eters   specified   by   the   State   under

§ 141.82(f) for more than nine days in any     six-month     period     specified     in

§ 141.87(d) shall conduct tap water sam- pling for lead and copper at the  fre- quency specified in paragraph (d)(3) of this section, collect the number of samples specified for standard moni- toring under paragraph (c) of this sec- tion, and shall resume monitoring for water quality parameters within the distribution  system  in  accordance  with

§ 141.87(d). This standard tap water sampling shall begin no later than the six-month period beginning January  1 of the calendar year following the lead action level  exceedance  or water  qual- ity parameter excursion. Such a sys- tem  may  resume  reduced  monitoring

#### 40 CFR Ch. I (7–1–17 Edition)

for lead and copper at the tap and for water quality parameters within the distribution system under the fol- lowing conditions:

- The system may resume annual monitoring for lead and copper at the tap at the reduced number of sites specified in paragraph (c) of this sec- tion after it has completed two subse- quent six-month rounds of monitoring that meet the criteria of paragraph (d)(4)(ii) of this section and the system has received written approval from the State that it is appropriate to resume reduced monitoring on an annual fre- quency. This sampling shall begin dur- ing the calendar year immediately fol- lowing the end of the second consecu- tive six-month monitoring period.

- The system may resume triennial monitoring for lead and copper at  the tap at the  reduced  number  of  sites after it demonstrates through subse- quent rounds of monitoring that it meets the criteria of either paragraph (d)(4)(iii) or (d)(4)(v) of this section and the system has received written ap- proval from the State that it is appro- priate  to  resume  triennial  monitoring.

- The system may reduce the num- ber  of  water  quality  parameter  tap water samples required in accordance with § 141.87(e)(1) and the frequency with which it collects such samples in accordance with § 141.87(e)(2). Such a system may not resume triennial mon- itoring for water quality parameters at the tap until it demonstrates, in ac- cordance    with    the    requirements    of

§ 141.87(e)(2), that it has re-qualified for triennial     monitoring.

(vii) Any water system subject to a reduced monitoring frequency under paragraph (d)(4) of this section shall notify the State in writing in accord- ance with § 141.90(a)(3) of any upcoming long-term change in treatment or addi- tion of a new source as described in that section.  The  State  must  review and approve the addition of a new source or long-term change in water treatment before it is implemented by the water system. The State may re- quire the system to resume sampling in accordance with paragraph  (d)(3)  of this section and collect the number of samples specified for standard moni- toring under paragraph (c) of this sec- tion  or  take  other  appropriate  steps

#### Environmental Protection Agency	§ 141.86

such as increased water quality param- eter monitoring or re-evaluation of its corrosion control treatment given the potentially different water quality con- siderations.

  - Additional monitoring by systems. The results of any monitoring con- ducted in addition to the minimum re- quirements of this section shall be con- sidered by the system and the State in making any determinations (i.e., calcu- lating the 90th percentile lead or cop- per level) under this subpart.

  - Invalidation of lead or copper tap water samples. A sample invalidated under this paragraph does not count to- ward determining lead or copper 90th percentile levels under § 141.80(c)(3) or toward meeting the minimum moni- toring requirements of paragraph (c) of this  section.

    - The State may invalidate  a  lead or copper tap water sample at least if one of the following conditions is met.

      - The laboratory establishes that improper sample analysis caused erro- neous results.

      - The State determines that the sample was taken from a site that did not meet the site selection criteria of this section.

      - The sample container was dam- aged in transit.

      - There is substantial reason to be- lieve that the sample was subject to tampering.

    - The system must report the re- sults of all samples to the State and all supporting documentation for samples the system  believes  should be  invali- dated.

    - To invalidate a sample under paragraph (f)(1) of this section, the de- cision and the rationale for the deci- sion must be documented in writing. States may not invalidate a sample solely on the grounds that a follow-up sample result is higher or lower than that of the original sample.

    - The water system must collect re- placement samples for any samples in- validated  under  this  section  if,  after the invalidation of one or more sam- ples, the system has too few samples to meet the minimum requirements of paragraph (c) of this section. Any such replacement samples must be taken as soon as possible, but no later than 20 days  after   the   date   the  State   invali-

dates the sample or by the end of the applicable monitoring period, which- ever occurs later. Replacement samples taken after the end of the applicable monitoring period shall not also be used to meet the monitoring require- ments of a subsequent monitoring pe- riod. The replacement samples shall be taken at the same locations as the in- validated samples or, if that is not pos- sible, at locations other than those al- ready used for sampling during the monitoring period.

  - Monitoring waivers for small sys- tems. Any small  system that meets the criteria of this paragraph may apply to the State to reduce the frequency of monitoring for lead and copper under this section to once every nine years (i.e., a ‘‘full waiver’’) if it meets  all  of the materials criteria specified in para- graph (g)(1) of this section and  all  of the monitoring criteria specified in paragraph (g)(2) of this section. If State regulations permit, any small system that meets the criteria in paragraphs (g)(1) and (2) of this section only for lead, or only for copper, may  apply  to the State for a waiver to reduce the frequency of tap water monitoring to once every nine years for that contami- nant only (i.e., a ‘‘partial waiver’’).

- Materials criteria. The system must demonstrate that its distribution sys- tem and service lines and all drinking water supply plumbing, including plumbing conveying drinking water within all residences and buildings con- nected to the system, are free of lead- containing materials and/or copper- containing materials, as those terms are defined in this paragraph, as fol- lows:

  - Lead. To qualify for a full waiver, or a waiver of the tap water moni- toring requirements for lead (i.e., a ‘‘lead waiver’’), the water system must provide certification and supporting documentation to the State that the system is free of all lead-containing materials, as follows:

    - It contains no plastic pipes which contain lead plasticizers, or plastic service lines which contain lead plasti- cizers; and

    - It is free of lead service lines, lead pipes, lead soldered pipe joints, and leaded brass or bronze alloy fit- tings and fixtures, unless such fittings

#### § 141.86

and  fixtures  meet  the  specifications  of any standard established pursuant to 42

U.S.C. 300g–6(e) (SDWA section 1417(e)).

  - Copper. To qualify for a full waiv- er, or a waiver of the tap water moni- toring requirements for copper (i.e., a ‘‘copper waiver’’), the water system must provide certification and sup- porting documentation to the  State that the system contains no copper pipes or copper service lines.

- Monitoring criteria for waiver issuance. The system must have com- pleted at least one 6-month round of standard tap water monitoring for lead and copper at sites approved by the State and from the number of sites re- quired by paragraph (c) of this section and demonstrate that the 90th per- centile levels for any and all rounds of monitoring conducted since the system became free of all lead-containing and/ or copper-containing materials, as ap- propriate, meet the following criteria.

- Lead levels. To qualify for a full waiver, or a lead waiver, the system must demonstrate that the 90th per- centile lead level does not exceed 0.005 mg/L.

- Copper levels. To qualify for a full waiver, or a copper waiver, the system must demonstrate that the 90th per- centile  copper  level  does  not  exceed

0.65 mg/L.

- State approval of waiver application. The State shall notify the system of its waiver determination, in writing, set- ting forth the basis of its decision and any condition of the waiver. As a con- dition of the waiver, the State may re- quire the system to perform specific activities (e.g., limited monitoring, periodic outreach to customers to re- mind them to avoid installation of ma- terials that might void the waiver) to avoid the risk of lead or copper con- centration of concern in tap water. The small system must continue moni- toring for lead and copper at the tap as required by paragraphs (d)(1) through (d)(4) of this section, as appropriate, until it receives written notification from the State that the waiver has been approved.

- Monitoring frequency for systems with waivers. (i) A system with a full waiver must conduct tap water moni- toring for lead and copper in accord- ance  with  paragraph  (d)(4)(iv)  of  this

#### 40 CFR Ch. I (7–1–17 Edition)

section at the reduced number of sam- pling sites identified in paragraph (c) of this section at least once every nine years and provide the materials certifi- cation specified in paragraph (g)(1) of this section for both lead and copper to the State along with the monitoring results. Samples collected every nine years shall be collected no later than every ninth calendar year.

- A system with a partial waiver must conduct tap water monitoring for the waived contaminant in accordance with paragraph (d)(4)(iv) of this section at the reduced number  of  sampling sites specified in paragraph (c) of this section at least once every nine years and provide the materials certification specified in paragraph (g)(1) of this sec- tion pertaining to the waived contami- nant along with the monitoring  re- sults. Such a system also must con- tinue to monitor for the non-waived contaminant in accordance with re- quirements of paragraph (d)(1) through (d)(4) of this section, as appropriate.

- Any water system with a full or partial waiver shall notify the State in writing in accordance with § 141.90(a)(3) of any upcoming long-term change in treatment or addition of  a  new  source, as described in that section. The State must review and approve  the  addition of a new source or long-term change in water treatment before it is imple- mented by the water system. The State has  the  authority  to  require  the  sys- tem to add or modify waiver conditions (e.g., require recertification that the system is free of  lead-containing and/or copper-containing materials, require additional round(s) of monitoring), if it deems such modifications are nec- essary to address treatment or source water  changes  at  the  system.

- If a system with a full or partial waiver becomes aware that it is no longer free of lead-containing or cop- per-containing materials, as appro- priate, (e.g., as a result of new con- struction or repairs), the system shall notify the State  in  writing  no  later than 60 days after becoming aware of such a change.

- Continued eligibility. If the system continues to satisfy the requirements of paragraph (g)(4) of this section, the waiver will be renewed automatically, unless any of the conditions listed in

#### Environmental Protection Agency	§ 141.87

paragraph (g)(5)(i) through (g)(5)(iii) of this section occurs. A system whose waiver has been revoked may re-apply for a waiver at such time as it again meets the appropriate materials and monitoring criteria of paragraphs (g)(1) and (g)(2) of this section.

  - A system with a full waiver or a lead waiver no longer satisfies the ma- terials criteria of paragraph (g)(1)(i) of this section or has a 90th percentile lead level greater than 0.005 mg/L.

  - A system with a full waiver or a copper waiver no longer satisfies the materials criteria of paragraph (g)(1)(ii) of this section or has a 90th percentile  copper  level  greater  than

0.65 mg/L.

  - The State notifies the system, in writing, that the waiver has been re- voked, setting forth the basis of its de- cision.

- Requirements following waiver rev- ocation. A system whose full or partial waiver has been  revoked  by  the  State is subject to the corrosion control treatment and lead and copper tap water monitoring requirements, as fol- lows:

  - If the system exceeds the lead and/ or copper action level, the system must implement  corrosion  control  treatment in accordance with the deadlines speci- fied in § 141.81(e), and any other appli- cable  requirements  of  this  subpart.

  - If the system meets both the lead and the copper action level, the system must monitor for lead and copper  at the tap no less frequently than once every three years using the reduced number of sample sites specified in paragraph (c) of this section.

- Pre-existing waivers. Small system waivers approved by the State in  writ- ing prior to April 11, 2000 shall remain in effect under the following condi- tions:

  - If the system has demonstrated that it is both free of lead-containing and copper-containing materials, as re- quired by paragraph (g)(1) of this sec- tion and that its 90th percentile lead levels and 90th percentile copper levels meet the criteria of paragraph (g)(2) of this section, the waiver remains in ef- fect so long as the system continues to meet the waiver eligibility criteria of paragraph (g)(5) of this section. The first   round   of   tap   water   monitoring

conducted pursuant to paragraph (g)(4) of this section shall be completed no later than nine  years  after  the  last time the system has monitored for lead and copper at the tap.

  - If the system has met the mate- rials criteria of paragraph (g)(1) of this section but has not met the monitoring criteria of paragraph (g)(2) of this sec- tion, the system shall conduct a round of monitoring for lead and copper  at the  tap  demonstrating  that  it  meets the criteria  of  paragraph  (g)(2) of  this section no later than September 30, 2000. Thereafter, the waiver shall re- main in effect as long as the system meets the continued eligibility  criteria of paragraph (g)(5) of this section. The first round of tap water monitoring conducted pursuant to paragraph (g)(4) of this section shall be completed no later than nine years after the round of monitoring conducted pursuant to paragraph (g)(2) of this section.

[56  FR 26548,  June 7,  1991;  56  FR 32113,  July

15, 1991; 57 FR 28788, June 29, 1992, as amend-

ed  at 65  FR 2007,  Jan. 12,  2000;  72  FR 57817,

Oct. 10, 2007]

##### § 141.87   Monitoring   requirements   for water quality parameters.

All large water systems, and all small- and medium-size systems that exceed the lead or copper action level shall monitor water quality param- eters in addition to lead and copper in accordance with this section. The re- quirements of this section are summa- rized in the table at the end of this sec- tion.

- General requirements—(1) Sample collection methods. (i) Tap samples shall be representative of water quality throughout the distribution system taking into account the number of per- sons served, the different sources of water, the different treatment methods employed by the system, and seasonal variability. Tap sampling under this section is not required to be conducted at taps targeted for lead and copper sampling under § 141.86(a). [Note: Sys- tems may find it convenient to conduct tap sampling for water quality param- eters at sites used for coliform sam- pling under 40 CFR 141.21.]

(ii) Samples collected at the entry point(s) to the distribution system shall be from locations representative

#### § 141.87

of each source after treatment. If a sys- tem draws water from more than one source and the sources are combined before distribution, the system must sample at an entry point to the dis- tribution system during periods of nor- mal operating conditions (i.e., when water is representative of all sources being used).

(2) Number of samples. (i) Systems shall collect two tap samples for appli- cable water quality parameters during each monitoring period specified under paragraphs (b) through (e) of this sec- tion from the following number  of sites.

| System size (No. people served) | No. of sites for water quality parameters |
| --- | --- |
| >100,000 ........................................................ | 25 |
| 10,001–100,000 ............................................. | 10 |
| 3,301 to 10,000 ............................................. | 3 |
| 501 to 3,300 .................................................. | 2 |
| 101 to 500 ..................................................... | 1 |
| 100 ............................................................... | 1 |

(ii) Except as provided in paragraph (c)(3) of this section, systems shall col- lect two samples for each applicable water quality parameter at each entry point to the distribution system during each monitoring period specified in paragraph (b) of this section. During each monitoring period specified in paragraphs (c)–(e) of this section, sys- tems shall collect one sample for each applicable water quality parameter at each entry point to the distribution system.

- Initial sampling All large water systems shall measure the applicable water quality parameters as specified below at taps and  at  each  entry  point to the distribution system during each six-month monitoring period specified in § 141.86(d)(1). All small and medium- size systems shall measure the applica- ble water quality parameters at the lo- cations specified below during each six- month  monitoring  period  specified  in

§ 141.86(d)(1) during which the system exceeds  the  lead  or  copper  action  level.

- At taps:

  - pH;

  - Alkalinity;

  - Orthophosphate, when an inhib- itor containing a  phosphate  compound is used;

  - Silica, when an inhibitor con- taining a silicate compound is used;

#### 40 CFR Ch. I (7–1–17 Edition)

  - Calcium;

  - Conductivity; and

  - Water temperature.

- At each entry point to the dis- tribution system: all of the applicable parameters listed in paragraph (b)(1) of this  section.

- Monitoring after installation of cor- rosion control. Any large system which installs optimal corrosion control treatment pursuant to § 141.81(d)(4) shall measure the water quality param- eters at the locations and frequencies specified below during each six-month monitoring       period       specified       in

§ 141.86(d)(2)(i). Any small or medium- size system which installs optimal cor- rosion control treatment shall conduct such monitoring during each six-month monitoring        period        specified        in

§ 141.86(d)(2)(ii) in which the system ex- ceeds the lead or copper action level.

  - At taps, two samples for:

    - pH;

    - Alkalinity;

    - Orthophosphate, when an inhib- itor containing a  phosphate  compound is used;

    - Silica, when an inhibitor con- taining a silicate compound is used;

    - Calcium, when calcium carbonate stabilization is used as part of corro- sion control.

  - Except as provided in paragraph (c)(3) of this section, at each entry point to the distribution system, at least one sample no less frequently than every two weeks (biweekly) for:

    - pH;

    - When alkalinity is adjusted as part of optimal corrosion control, a reading of the dosage rate of the chem- ical used to adjust alkalinity, and the alkalinity concentration; and

    - When a corrosion inhibitor is used as part of optimal corrosion con- trol, a reading of the dosage rate of the inhibitor used, and the  concentration of orthophosphate  or  silica (whichever is applicable).

  - Any ground water system can limit entry point sampling described in paragraph (c)(2) of this section to those entry points that are representative of water quality and treatment condi- tions throughout the system. If water from untreated ground water sources mixes  with  water  from  treated  ground

#### Environmental Protection Agency	§ 141.87

water sources, the system must mon- itor for water quality  parameters  both at representative entry points receiv- ing treatment and representative entry points receiving no treatment. Prior to the start of any monitoring under this paragraph, the system shall provide to the State written information identi- fying the selected entry points and doc- umentation, including information on seasonal variability, sufficient to dem- onstrate that the sites are representa- tive of water quality and treatment conditions throughout the system.

- Monitoring after State specifies water quality parameter values for opti- mal corrosion control. After the State specifies the values for applicable water quality control parameters re- flecting optimal corrosion control treatment under § 141.82(f), all large systems shall measure the applicable water quality parameters in accord- ance with paragraph (c) of this section and determine compliance with the re- quirements of § 141.82(g) every six months with the first six-month period to begin on either January 1 or July 1, whichever comes first, after the State specifies   the   optimal   values   under

§ 141.82(f). Any small or medium-size system shall conduct such monitoring during each six-month period specified in this paragraph in which the system exceeds the lead or copper action level. For any such small and medium-size system that is subject to a reduced monitoring     frequency     pursuant     to

§ 141.86(d)(4) at the time of the action level exceedance, the start of the appli- cable six-month monitoring period under this paragraph shall coincide with the start of the applicable moni- toring period under § 141.86(d)(4). Com- pliance with State-designated optimal water  quality  parameter  values  shall be    determined    as    specified    under

§ 141.82(g).

- Reduced monitoring. (1) Any water system that maintains the range of values for the water quality  param- eters reflecting optimal corrosion con- trol treatment during each of two con- secutive six-month monitoring periods under paragraph (d) of  this  section shall continue monitoring at the entry point(s) to the distribution system as specified in paragraph (c)(2) of this sec- tion.  Such  system  may  collect  two  tap

samples for applicable water quality parameters from the following reduced number of sites during each six-month monitoring period.

| System size (No. of people served) | Reduced No. of sites for water quality parameters |
| --- | --- |
| >100,000 ........................................................ | 10 |
| 10,001 to 100,000 ......................................... | 7 |
| 3,301 to 10,000 ............................................. | 3 |
| 501 to 3,300 .................................................. | 2 |
| 101 to 500 ..................................................... | 1 |
| 100 ............................................................... | 1 |

(2)(i) Any water system that main- tains the range of values for the water quality parameters reflecting optimal corrosion control  treatment  specified by the State under § 141.82(f) during three consecutive years of monitoring may reduce the  frequency  with  which it collects the number of tap  samples for applicable water quality param- eters specified in this paragraph (e)(1) of this section from  every  six  months to annually. This sampling begins dur- ing the calendar year immediately fol- lowing the end of the monitoring pe- riod in which the  third  consecutive year of six-month monitoring occurs. Any water system that maintains the range of values for the water quality parameters reflecting optimal corro- sion control treatment specified by the State under § 141.82(f), during three consecutive years of annual monitoring under this paragraph may reduce the frequency with which it collects the number of tap samples for applicable water quality parameters specified in paragraph (e)(1) of this section from annually to every three years. This sampling begins no later than the third calendar year following the end of the monitoring period in which the third consecutive  year  of  monitoring  occurs.

(ii) A water system may reduce the frequency with which it collects tap samples for applicable water quality parameters specified in paragraph (e)(1) of this section to every three years if it demonstrates during two consecutive monitoring periods that  its  tap  water lead level at the 90th percentile is less than or equal to the PQL for lead speci- fied in § 141.89 (a)(1)(ii), that its tap water copper level at the 90th per- centile is less than or equal to 0.65 mg/ L for copper in § 141.80(c)(2), and that it

#### § 141.87

also has maintained the range of values for the water quality parameters re- flecting optimal corrosion control treatment specified by the State under

§ 141.82(f). Monitoring conducted every three years shall be done no later than every third calendar year.

- A water system that conducts sampling annually shall collect these samples evenly throughout the year so as to reflect seasonal variability.

- Any water system subject to the reduced monitoring  frequency  that fails to operate at or above the min- imum value or within the range of val- ues for the water quality parameters specified by the State in § 141.82(f) for more than  nine days in  any six-month period specified in § 141.82(g) shall re- sume distribution system tap water sampling in accordance with the num- ber and frequency requirements in paragraph (d) of this section. Such a system may resume annual monitoring

#### 40 CFR Ch. I (7–1–17 Edition)

for water quality parameters at the tap at the reduced number of sites speci- fied in paragraph (e)(1) of this section after it  has  completed  two subsequent consecutive six-month rounds of moni- toring that meet the criteria of that paragraph and/or may resume triennial monitoring for water quality param- eters at the tap at the reduced number of sites after it demonstrates through subsequent rounds of  monitoring  that it meets the criteria of either  para- graph (e)(2)(i) or (e)(2)(ii) of this sec- tion.

- Additional monitoring by systems. The results of any monitoring con- ducted in addition to the minimum re- quirements of this section shall be con- sidered by the system and the State in making any determinations (i.e., deter- mining concentrations of water quality parameters)   under   this   section   or

§ 141.82.

SUMMARY OF MONITORING REQUIREMENTS FOR WATER QUALITY PARAMETERS 1

| Monitoring period | Parameters 2 | Location | Frequency |
| --- | --- | --- | --- |
| Initial monitoring ................. After installation of corro- sion control. After State specifies param- eter values for optimal corrosion control. Reduced monitoring ........... | pH, alkalinity, orthophosphate or sili- ca 3, calcium, conductivity, tempera- ture. pH, alkalinity, orthophosphate or sili- ca 3, calcium 4. pH, alkalinity, dosage rate and con- centration (if alkalinity adjusted as part of corrosion control), inhibitor dosage rate and inhibitor residual 5. pH, alkalinity, orthophosphate or sili- ca 3, calcium 4. pH, alkalinity dosage rate and con- centration (if alkalinity adjusted as part of corrosion control), inhibitor dosage rate and inhibitor residual 5. pH, alkalinity, orthophosphate or sili- ca 3, calcium 4. pH, alkalinity dosage rate and con- centration (if alkalinity adjusted as part of corrosion control), inhibitor dosage rate and inhibitor residual 5. | Taps and at entry point(s) to distribution system. Taps ................................... Entry point(s) to distribution system 6. Taps ................................... Entry point(s) to distribution system 6. Taps ................................... Entry point(s) to distribution system 6. | Every 6 months. Every 6 months. No less frequently than every two weeks. Every 6 months. No less frequently than every two weeks. Every 6 months, annually 7 or every 3 years 8; re- duced number of sites. No less frequently than every two weeks. |

1 Table is for illustrative purposes; consult the text of this section for precise regulatory requirements.

2 Small and medium-size systems have to monitor for water quality parameters only during monitoring periods in which the system exceeds the lead or copper action level.

3 Orthophosphate must be measured only when an inhibitor containing a phosphate compound is used. Silica must be meas- ured only when an inhibitor containing silicate compound is used.

4 Calcium must be measured only when calcium carbonate stabilization is used as part of corrosion control.

5 Inhibitor dosage rates and inhibitor residual concentrations (orthophosphate or silica) must be measured only when an inhib- itor is used.

6 Ground water systems may limit monitoring to representative locations throughout the system.

7 Water systems may reduce frequency of monitoring for water quality parameters at the tap from every six months to annually if they have maintained the range of values for water quality parameters reflecting optimal corrosion control during 3 consecutive years of monitoring.

8 Water systems may further reduce the frequency of monitoring for water quality parameters at the tap from annually to once every 3 years if they have maintained the range of values for water quality parameters reflecting optimal corrosion control during 3 consecutive years of annual monitoring. Water systems may accelerate to triennial monitoring for water quality parameters at the tap if they have maintained 90th percentile lead levels less than or equal to 0.005 mg/L, 90th percentile copper levels less than or equal to 0.65 mg/L, and the range of water quality parameters designated by the State under § 141.82(f) as representing optimal corrosion control during two consecutive six-month monitoring periods.

#### Environmental Protection Agency	§ 141.88

[56 FR 26548, June 7, 1991; 57 FR 28788, June 29, 1992, as amended at 59 FR 33862, June 30, 1994;

65 FR 2010, Jan. 12, 2000; 72 FR 57818, Oct. 10, 2007]

##### § 141.88   Monitoring   requirements   for lead and copper in source water.

- Sample location, collection methods, and number of samples. (1) A water sys- tem that fails to meet the lead or cop- per action level on the basis of tap samples  collected  in  accordance  with

§ 141.86 shall collect lead and copper source  water  samples  in  accordance with the following requirements re- garding sample location, number of samples,  and  collection  methods:

- Groundwater systems shall take a minimum of one sample at every entry point to the distribution system which is representative of each well after treatment (hereafter called a sampling point). The system shall take one sam- ple at the same sampling point unless conditions make  another  sampling point more representative of each source or treatment plant.

- Surface water systems shall take a minimum of one sample at every entry point to the distribution system after any application of  treatment  or in the distribution system at a point which is representative of each source after treatment (hereafter called a sampling point). The system shall take each sample at the same  sampling point unless conditions make another sampling point more representative of each source or treatment plant.

NOTE TO PARAGRAPH (a)(1)(ii): For the pur- poses of this paragraph, surface water sys- tems include systems with a combination of surface and ground sources.

- If a system draws water from more than one source and the sources are combined before distribution, the system must sample at  an  entry  point to the distribution system during peri- ods of normal operating conditions (i.e., when water is representative of all sources being used).

- The State may reduce the total number of samples which must be ana- lyzed by allowing the use of compositing. Compositing of samples must be done by certified laboratory personnel. Composite samples from a maximum of five samples are allowed, provided that if the lead concentration in  the  composite  sample  is  greater

than or equal to 0.001 mg/L or the cop- per concentration is greater than or equal to 0.160 mg/L, then either:

- A follow-up sample shall be taken and analyzed within 14 days at each sampling point included in the com- posite; or

- If duplicates of or sufficient quan- tities from the original samples from each sampling point used in the com- posite are available, the system may use these instead of resampling.

(2) Where the results of sampling in- dicate an exceedance of maximum per- missible source water levels estab- lished under § 141.83(b)(4), the State may require that one additional sample be collected as soon as possible  after the initial sample was  taken  (but  not to exceed two weeks) at the same sam- pling point. If a State-required con- firmation sample is taken for lead or copper, then the results of the initial and confirmation sample shall be aver- aged in determining compliance with the State-specified maximum permis- sible levels. Any sample value below the detection limit shall  be  considered to be zero. Any value above the detec- tion limit but below the PQL shall ei- ther be considered as the measured value or be considered  one-half  the PQL.

- Monitoring frequency after system exceeds tap water action level. Any sys- tem which exceeds the lead or copper action level at the tap shall collect one source water sample from each entry point to the distribution  system  no later than six months after the  end  of the monitoring period during which the lead or copper action level was exceed- ed. For monitoring periods that are an- nual or less frequent, the end of the monitoring period is September 30 of the calendar year in which the sam- pling occurs, or if the State has estab- lished an alternate monitoring period, the last day of that period.

- Monitoring frequency after installa- tion of source water treatment. Any sys- tem which installs source water treat- ment pursuant to § 141.83(a)(3) shall col- lect an additional source water sample from each entry point to the distribu- tion   system   during   two   consecutive

#### § 141.89

six-month   monitoring   periods   by   the deadline specified in § 141.83(a)(4).

- Monitoring frequency after State specifies maximum permissible source water levels or determines that source water treatment is not needed. (1) A sys- tem shall monitor at the frequency specified below in cases where  the State specifies maximum permissible source water levels under § 141.83(b)(4) or determines that the system is not required to install source water treat- ment under § 141.83(b)(2).

- A water system using only groundwater shall collect samples once during the three-year compliance  pe- riod (as that term  is  defined  in  § 141.2) in effect when the applicable State de- termination under  paragraph (d)(1) of this  section  is  made.   Such   systems shall collect samples once during each subsequent compliance period.  Tri- ennial samples shall be collected every third  calendar  year.

- A water system using surface water (or a combination of surface and ground water) shall collect samples once during each calendar year, the first annual monitoring period to begin during the year in which the applicable State determination is made under paragraph (d)(1) of this section.

(2) A system is not required to con- duct source water sampling for lead and/or copper if the system meets the action level for the specific contami- nant in tap water samples during the entire source water sampling period ap- plicable to the system under paragraph (d)(1) (i) or (ii) of this section.

- Reduced monitoring frequency. (1) A water system using only ground water may reduce the monitoring frequency for lead and copper in source water to once during each nine-year compliance cycle (as that term is defined in § 141.2) provided that the samples are collected no later than every ninth calendar year and if the system meets one of the fol- lowing  criteria:

- The system demonstrates that fin- ished drinking water entering the dis- tribution system has been maintained below the maximum  permissible  lead and copper concentrations specified by the State in § 141.83(b)(4) during at least three consecutive compliance periods under paragraph (d)(1) of  this  section; or

#### 40 CFR Ch. I (7–1–17 Edition)

- The State has determined that source water treatment is not needed and the system demonstrates that, dur- ing at least three consecutive compli- ance periods in which sampling was conducted under paragraph (d)(1) of this section, the concentration  of  lead in source water was less than or equal to 0.005 mg/L and the concentration of copper in source water was less than or equal to 0.65 mg/L.

- A water system using surface water (or a combination of surface water and ground water) may reduce the monitoring frequency in paragraph (d)(1) of this section to once during each nine-year compliance cycle  (as that term is defined in § 141.2) provided that the samples are collected no later than every ninth calendar year and  if the system meets one of the following criteria:

- The system demonstrates that fin- ished drinking water entering the dis- tribution system has been maintained below the maximum permissible lead and copper concentrations specified by the State in § 141.83(b)(4) for at least three consecutive years; or

- The State has determined that source water treatment is not needed and the system demonstrates that, dur- ing at least three consecutive years, the concentration of lead in source water was less than or equal to 0.005 mg/L and the concentration of copper in source water was less than or equal to 0.65 mg/L.

- A water system that uses a new source of water is not eligible for re- duced monitoring for lead and/or cop- per until concentrations in samples collected from the new source during three consecutive monitoring  periods are below the maximum  permissible lead and copper concentrations speci- fied by the State in § 141.83(a)(5).

[56  FR  26548,  June  7,  1991;  57  FR  28788  and

28789, June 29, 1992, as amended at 65 FR 2012,

Jan. 12, 2000; 72 FR 57819, Oct. 10, 2007]

##### § 141.89   Analytical methods.

  - Analyses for lead, copper, pH, con- ductivity,	calcium,	alkalinity, orthophosphate, silica, and tempera- ture shall be conducted with the meth- ods in § 141.23(k)(1).

#### Environmental Protection Agency	§ 141.90

    - Analyses for alkalinity, calcium, conductivity, orthophosphate, pH, sili- ca, and temperature may be performed by any person acceptable to the State. Analyses under this  section  for  lead and copper shall only be conducted by laboratories that have been certified by EPA or the State. To obtain  certifi- cation to conduct analyses for lead and copper, laboratories must:

      - Analyze Performance Evaluation samples, which include lead and cop- per, provided by or acceptable to EPA or the State at least once a year by each method for which the laboratory desires certification; and

      - Achieve quantitative acceptance limits as follows:

        - For lead: 30 percent of the actual amount in the Performance Evaluation sample when the actual  amount  is greater than  or  equal  to  0.005  mg/L. The  Practical  Quantitation  Level,   or PQL for lead is 0.005 mg/L.

        - For Copper: 10 percent of the ac- tual amount in the Performance Eval- uation sample when  the  actual  amount is greater than or equal to 0.050  mg/L. The  Practical  Quantitation  Level,   or PQL for copper is 0.050 mg/L.

      - Achieve the method detection limit for lead of 0.001 mg/L according to the procedures in appendix B of part 136 of this title. This need only be ac- complished if the laboratory will be processing source water composite samples under § 141.88(a)(1)(iv).

      - Be currently certified by EPA or the State to perform analyses to the specifications described in paragraph (a)(1) of this section.

    - States have the authority to allow the use of previously collected moni- toring data for purposes of monitoring, if the data were collected and analyzed in accordance with the requirements of this  subpart.

    - All lead and copper levels meas- ured between the PQL and  MDL  must be either reported as measured or they can be reported as one-half the PQL specified for lead and copper in para- graph (a)(1)(ii) of this section. All lev- els below the lead and copper MDLs must be reported as zero.

    - All copper levels measured be- tween the PQL and the MDL must be either reported as measured or they can  be  reported  as  one-half  the  PQL

(0.025 mg/L). All levels below the copper MDL must be reported as zero.

  - [Reserved]

[56 FR 26548, June 7, 1991, as amended at 57

FR 28789, June 29, 1992; 57 FR 31847, July 17,

1992; 59 FR 33863, June 30, 1994; 59 FR 62470,

Dec. 5,  1994;  64  FR 67466,  Dec. 1,  1999;  65  FR

2012, Jan. 12, 2000; 72 FR 57819, Oct. 10, 2007]

##### § 141.90   Reporting requirements.

All water systems shall report all of the following information to the State in accordance with this section.

(a) Reporting requirements for tap water monitoring for lead and copper and for  water  quality  parameter  monitoring.

- Except as provided in paragraph (a)(1)(viii) of this section, a water sys- tem shall report the information speci- fied below for all tap water samples specified in § 141.86 and for all water quality  parameter  samples  specified  in

§ 141.87 within the first 10 days fol- lowing the end of each applicable moni- toring  period  specified  in  § 141.86  and

§ 141.87 (i.e., every six months, annu- ally, every 3 years, or every 9  years). For monitoring periods with a duration less than six months, the end of the monitoring period is the last date sam- ples can be collected  during  that  period as specified in §§ 141.86 and 141.87.

  - The results of all tap samples for lead and copper including the location of  each  site  and  the  criteria  under

§ 141.86(a)   (3),   (4),   (5),   (6),   and/or   (7)

under which the site was selected  for the system’s sampling pool;

  - Documentation for each tap water lead or copper sample for which the water system requests invalidation pursuant to § 141.86(f)(2);

  - [Reserved]

  - The 90th percentile lead and cop- per concentrations measured  from among all lead and copper tap water samples collected during each moni- toring period (calculated in accordance with § 141.80(c)(3)), unless the State cal- culates the system’s 90th  percentile lead and copper levels under paragraph

  - of this section;

  - With the exception of initial tap sampling     conducted     pursuant     to

§ 141.86(d)(1), the system shall designate any site which was not sampled during previous monitoring periods, and in- clude an explanation of why sampling sites have changed;

#### § 141.90

  - The results of all tap samples for pH, and where applicable, alkalinity, calcium,   conductivity,   temperature, and orthophosphate or silica collected under § 141.87 (b)–(e);

  - The results of all samples col- lected at the entry point(s) to the dis- tribution system for applicable water quality parameters under § 141.87 (b)– (e);

  - A water system shall report the results of all water quality parameter samples collected under § 141.87(c) through (f) during each six-month mon- itoring period specified in § 141.87(d) within the first 10 days following the end of the monitoring period unless the State has specified a more frequent re- porting   requirement.

- For a non-transient non-commu- nity water system, or a community water  system  meeting  the  criteria  of

§ 141.85(b)(7), that does not have enough taps that can provide  first-draw  sam- ples,  the  system  must  either:

  - Provide written documentation  to the  State  identifying   standing   times and locations for enough non-first-draw samples to make up its sampling pool under § 141.86(b)(5) by the start of the first  applicable  monitoring   period under § 141.86(d) that commences after April 11, 2000, unless the State has waived prior State approval of non- first-draw sample sites selected by the system pursuant to § 141.86(b)(5); or

  - If the State has waived prior ap- proval of non-first-draw sample sites selected by the system, identify, in writing, each site that did not meet the six-hour minimum standing time and the length of standing time for that particular substitute sample collected pursuant to § 141.86(b)(5) and include this information with the lead and cop- per tap sample results required to be submitted pursuant to paragraph (a)(1)(i) of this section.

- At a time specified by the State, or if no specific time is designated by the State, then as early as possible prior to the addition of a new source or any long-term change in water treat- ment, a water system deemed to have optimized    corrosion    control    under

§ 141.81(b)(3), a water system subject to reduced      monitoring      pursuant      to

§ 141.86(d)(4), or a water system subject to   a   monitoring   waiver   pursuant   to

#### 40 CFR Ch. I (7–1–17 Edition)

§ 141.86(g), shall submit written docu- mentation to the State describing the change or addition. The State must re- view and approve the addition of a new source or long-term change in treat- ment before it is implemented by the water system. Examples of long-term treatment changes include the addition of a new treatment process or modi- fication of an existing treatment proc- ess. Examples of modifications include switching secondary disinfectants, switching coagulants (e.g., alum to fer- ric chloride), and switching corrosion inhibitor	products	(e.g., orthophosphate to blended phosphate). Long-term changes can include dose changes to existing chemicals if the system is planning long-term  changes to its finished water pH or residual in- hibitor concentration. Long-term treatment changes would not include chemical dose fluctuations associated with daily raw water quality changes.

- Any small system applying for a monitoring waiver under § 141.86(g), or subject to a waiver granted pursuant to

§ 141.86(g)(3), shall provide the following information to the State in writing  by the  specified  deadline:

  - By the start of the first applicable monitoring period in § 141.86(d), any small water system applying for a monitoring waiver shall provide the documentation required to dem- onstrate that it meets the waiver cri- teria of §§ 141.86(g)(1) and (2).

  - No later than nine years after the monitoring previously conducted pur- suant to § 141.86(g)(2) or § 141.86(g)(4)(i), each small system desiring to  maintain its monitoring waiver shall provide the information required by §§ 141.86(g)(4)(i) and  (ii).

  - No later than 60 days after it be- comes aware that it is no longer free of lead-containing and/or copper-con- taining material, as appropriate, each small system with a monitoring waiver shall provide  written  notification  to the State, setting forth the cir- cumstances resulting in the lead-con- taining and/or copper-containing mate- rials being introduced into the system and what corrective action, if any, the system plans to remove these mate- rials.

  - By October 10, 2000, any small system  with  a  waiver  granted  prior  to

#### Environmental Protection Agency	§ 141.90

April 11, 2000 and that has not pre- viously      met      the      requirements      of

§ 141.86(g)(2) shall provide the informa- tion   required   by   that   paragraph.

- Each ground water system that limits water quality parameter moni- toring to a subset of entry points under

§ 141.87(c)(3) shall provide, by the com- mencement of  such  monitoring,  writ- ten correspondence to the State that identifies the selected entry points and includes information sufficient to dem- onstrate that the sites are representa- tive of water quality and treatment conditions  throughout  the  system.

- Source water monitoring reporting requirements. (1) A water system shall report the sampling results for all source water samples collected in ac- cordance with § 141.88 within the first 10 days following the end of each source water monitoring period (i.e., annually, per compliance period, per compliance cycle) specified in § 141.88.

(2) With the exception of the  first round of source water sampling con- ducted pursuant to § 141.88(b), the sys- tem  shall  specify  any  site  which  was not sampled during previous  moni- toring periods, and include an expla- nation of why the sampling point has changed.

- Corrosion control treatment report- ing  requirements.  By  the   applicable dates under § 141.81, systems shall re- port  the  following  information:

  - For systems demonstrating that they have already optimized corrosion control,     information     required     in

§ 141.81(b) (2) or (3).

  - For systems required to optimize corrosion control,  their  recommenda- tion regarding optimal corrosion con- trol treatment under § 141.82(a).

  - For systems required to evaluate the effectiveness of corrosion control treatments under § 141.82(c), the infor- mation required by that paragraph.

  - For systems required to install optimal corrosion control designated by the State under § 141.82(d), a letter certifying that the system has com- pleted installing that treatment.

- Source water treatment reporting re- quirements.  By  the  applicable  dates  in

§ 141.83, systems shall provide the fol- lowing information to the State:

    - If required under § 141.83(b)(1), their    recommendation    regarding source  water  treatment;

    - For systems required to install source       water       treatment       under

§ 141.83(b)(2), a  letter  certifying  that the system  has  completed  installing the treatment designated by the State within 24 months after the State des- ignated  the  treatment.

- Lead service line replacement report- ing requirements.  Systems  shall  report the following information to  the  State to demonstrate compliance with the re- quirements of § 141.84:

  - No later than 12 months after the end of a monitoring period in which a system exceeds the lead action level in sampling referred to in § 141.84(a), the system must submit written docu- mentation to the State of the material evaluation   conducted   as   required   in

§ 141.86(a), identify the initial  number of lead service lines in its distribution system at the time the system exceeds the lead action level, and provide the system’s schedule for annually replac- ing at least 7 percent of the initial number of lead service lines in its dis- tribution  system.

  - No later than 12 months after the end of a monitoring period in which a system exceeds the lead action level in sampling referred to in § 141.84(a), and every 12 months thereafter, the system shall demonstrate to the State in writ- ing that the system has either:

- Replaced in the previous 12 months at least 7 percent of the initial lead service lines (or a greater number of  lines  specified  by  the  State  under

§ 141.84(e)) in its distribution system, or

- Conducted sampling which dem- onstrates that the lead  concentration in all service line samples from an indi- vidual    line(s),    taken    pursuant    to

§ 141.86(b)(3),   is   less   than   or   equal   to

0.015 mg/L. In such cases, the total number of lines replaced and/or which meet the  criteria in  § 141.84(c) shall equal at least 7 percent of the initial number of lead lines identified under paragraph (e)(1) of this section (or the percentage specified by the State under

§ 141.84(e)).

  - The annual letter submitted to the State under paragraph (e)(2) of this section shall contain the following in- formation:

#### § 141.90

    - The number of lead service lines scheduled to be replaced during the previous year of the system’s replace- ment schedule;

    - The number and location of each lead service line replaced during the previous year of the system’s replace- ment schedule;

    - If measured, the water lead con- centration and location of each lead service line sampled, the sampling method, and the date of sampling.

  - Any system which collects lead service line samples following partial lead service line replacement required by § 141.84 shall report the results to the State within the first ten  days  of the month following the month in which the system receives the labora- tory results, or as specified  by  the State. States, at their discretion may eliminate this requirement to report these  monitoring  results.   Systems shall also report any additional infor- mation as specified by  the  State,  and in a time and manner prescribed by the State, to verify that all partial lead service  line  replacement   activities have taken place.

- Public education program reporting requirements. (1) Any water  system  that is subject to the public education re- quirements in § 141.85 shall, within ten days after the end of  each  period  in which the system  is  required  to  per- form public  education in  accordance with § 141.85(b), send written docu- mentation  to  the  State  that  contains:

- A demonstration  that  the  system has delivered the public education ma- terials that meet the content require- ments in § 141.85(a) and the delivery re- quirements in § 141.85(b); and

- A list of all the newspapers, radio stations, television stations, and facili- ties and organizations to which the system delivered public education ma- terials during the period in which the system was required to perform public education tasks.

      - Unless required by the State, a system that previously has submitted the information required by paragraph (f)(1)(ii) of this section need not resub- mit the information required by para- graph (f)(1)(ii) of this section, as long as there have been no changes in the distribution list and the system cer- tifies that the public education mate-

#### 40 CFR Ch. I (7–1–17 Edition)

rials were distributed to the same list submitted previously.

      - No later than 3 months following the end of the monitoring period, each system must mail a sample copy of the consumer notification of tap results to the State along  with  a  certification that the notification has been distrib- uted in a manner consistent with the requirements of § 141.85(d).

- Reporting of additional monitoring data. Any system which collects sam- pling data in addition to  that  required by this subpart shall  report  the  results to the State within the first ten days following the end of the applicable monitoring period under §§ 141.86, 141.87 and 141.88 during which the samples are collected.

- Reporting of 90th percentile lead and copper concentrations where  the State calculates a system’s 90th percentile concentrations. A water system is not required to report the 90th percentile lead and copper concentrations meas- ured from among all lead and  copper tap water samples collected during each monitoring period, as required by paragraph (a)(1)(iv) of this section if:

- The State has previously notified the water system that it will calculate the water system’s 90th percentile lead and copper concentrations, based on the lead and copper tap results sub- mitted pursuant to paragraph (h)(2)(i) of this section, and has specified a date before the end of the applicable moni- toring period by which the system must provide the results of lead and copper tap water samples;

- The system has provided the fol- lowing information to the State by the date specified in paragraph (h)(1) of this section:

  - The results of all tap samples for lead and copper including the location of  each  site  and  the  criteria  under

§ 141.86(a)(3), (4), (5), (6), and/or (7) under which the site was selected for the sys- tem’s sampling pool, pursuant to para- graph (a)(1)(i) of this section; and

  - An identification of sampling sites utilized during the current moni- toring period that were not sampled during previous monitoring periods, and an explanation why sampling sites have changed; and

- The State has provided the results of the 90th percentile lead and copper

#### Environmental Protection Agency	§ 141.111

calculations, in writing, to the water system before the end of the moni- toring period.

[56  FR  26548,  June  7,  1991;  57  FR  28789,  June

29, 1992, as amended at 59 FR 33864, June 30,

1994;  65  FR 2012,  Jan. 12,  2000;  72  FR 57819,

Oct. 10, 2007]

##### § 141.91   Recordkeeping requirements.

Any system subject to the require- ments  of  this  subpart  shall   retain   on its premises original records of all sampling data and analyses, reports, surveys,  letters,  evaluations,   sched- ules, State determinations,  and  any other information required by §§ 141.81 through 141.88. Each water system shall retain the records required by this sec- tion for no fewer than 12 years.

# Subpart J—Use of Non-Centralized Treatment Devices

SOURCE: 52  FR 25716,  July 8, 1987,  unless

otherwise noted.

##### § 141.100 Criteria and procedures for public water systems using point-of- entry devices.

- Public water systems may use point-of-entry devices to comply with maximum contaminant levels only if they meet the requirements of this sec- tion.

- It is the responsibility of the pub- lic water system to operate and main- tain the point-of-entry treatment sys- tem.

- The public water system must de- velop and obtain State approval for a monitoring plan before point-of-entry devices are installed for compliance. Under the plan approved by the State, point-of-entry devices must provide health protection equivalent to central water treatment. ‘‘Equivalent’’ means that the water would meet all national primary drinking water regulations and would be of acceptable quality similar to water distributed by a well- operated central treatment plant. In addition to the VOCs, monitoring must include physical measurements and ob- servations such as total flow treated and mechanical condition of the treat- ment equipment.

- Effective technology must be properly applied under a plan approved by  the  State  and  the  microbiological

safety  of  the  water  must  be  main- tained.

- The State must require adequate certification of performance, field test- ing, and, if not included in the certifi- cation process, a rigorous engineering design review of the point-of-entry de- vices.

- The design and application of the point-of-entry devices must consider the tendency for increase in heterotrophic bacteria concentrations in water treated with activated carbon. It may be necessary to use frequent backwashing, post-contactor disinfec- tion, and Heterotrophic Plate Count monitoring to ensure that the micro- biological safety of the water is not compromised.

- All consumers shall be protected. Every building connected to the sys- tem must have a point-of-entry device installed, maintained, and adequately monitored. The State must be assured that every building is subject to treat- ment and monitoring, and that the rights and responsibilities of the public water system customer convey with title upon sale of property.

[52 FR 25716, July 8, 1987; 53 FR 25111, July 1,

1988]

##### § 141.101   Use of bottled water.

Public water systems shall not use bottled water to achieve compliance with an MCL. Bottled water may be used on a temporary basis to avoid un- reasonable risk to health.

[63 FR 31934, June 11, 1998]

# Subpart K—Treatment Techniques

SOURCE: 56  FR 3594,  Jan. 30,  1991,  unless

otherwise noted.

##### § 141.110   General requirements.

The requirements of subpart K of this part constitute national primary drinking water regulations. These reg- ulations establish treatment tech- niques in lieu of maximum contami- nant levels for specified contaminants.

##### § 141.111   Treatment techniques for ac- rylamide and epichlorohydrin.

Each public water system must cer- tify annually in writing to the State (using  third  party  or  manufacturer’s

§ 141.130

certification)  that  when  acrylamide and epichlorohydrin are used in drink- ing water systems, the combination (or product) of dose and monomer level does not exceed the levels specified as follows:

Acrylamide = 0.05% dosed at 1 ppm (or equiv- alent)

Epichlorohydrin = 0.01% dosed at 20 ppm (or equivalent)

Certifications can rely on manufactur- ers or third parties, as approved by the State.

# Subpart L—Disinfectant Residuals, Disinfection Byproducts, and Disinfection Byproduct Precur- sors

##### § 141.130   General requirements.

  - The requirements of this subpart L constitute national primary drinking water regulations.

    - The regulations in this subpart es- tablish criteria under which  commu- nity water systems (CWSs) and non- transient,  noncommunity  water   sys- tems (NTNCWSs) which add a chemical disinfectant to the water in any  part  of the drinking water treatment process must modify their practices to meet MCLs and MRDLs in §§ 141.64 and 141.65, respectively, and must meet the treat- ment technique requirements for dis- infection      byproduct      precursors      in

§ 141.135.

    - The regulations in this subpart es- tablish criteria under which transient NCWSs that use chlorine dioxide as a disinfectant  or  oxidant  must  modify their practices to meet the MRDL for chlorine dioxide in § 141.65.

    - EPA   has   established   MCLs   for TTHM  and  HAA5  and  treatment  tech- nique requirements for disinfection by- product  precursors  to  limit  the  levels of known and unknown disinfection by- products    which    may    have    adverse health   effects.   These   disinfection   by- products	may	include	chloroform; bromodichloromethane; dibromochloromethane;	bromoform; dichloroacetic  acid;  and  trichloroacetic acid.

  - Compliance dates—(1) CWSs and NTNCWSs. Unless otherwise noted, sys- tems must comply with the require- ments of this subpart as follows. Sub-

40 CFR Ch. I (7–1–17 Edition)

part H systems serving 10,000 or more persons must comply with this subpart beginning January 1, 2002. Subpart H systems serving fewer than 10,000 per- sons and systems using only ground water not under the direct influence of surface water must comply with this subpart beginning January 1, 2004.

(2) Transient NCWSs. Subpart H sys- tems serving 10,000 or more persons and using chlorine dioxide as  a  disinfectant or oxidant must comply with any re- quirements for chlorine dioxide in this subpart beginning January 1, 2002. Sub- part H systems serving  fewer  than 10,000 persons and using chlorine diox- ide as a disinfectant or oxidant and systems using only ground water not under the direct influence of surface water and using chlorine dioxide as a disinfectant  or  oxidant  must  comply with any requirements for chlorine di- oxide  in  this  subpart  beginning  Janu- ary 1, 2004.

  - Each CWS and NTNCWS regulated under paragraph (a) of this  section must be operated by qualified per- sonnel who meet the requirements specified by the State and are included in a State register of qualified opera- tors.

  - Control of disinfectant residuals. Notwithstanding the MRDLs in § 141.65, systems may increase residual dis- infectant levels in the distribution sys- tem of chlorine or chloramines (but not chlorine dioxide) to a level and for a time   necessary   to   protect   public health, to address specific micro- biological  contamination  problems caused by  circumstances  such  as,  but not limited to, distribution line breaks, storm run-off events, source water con- tamination events, or cross-connection events.

[63 FR 69466, Dec. 16, 1998, as amended at 66

FR 3776, Jan. 16, 2001]

##### § 141.131   Analytical requirements.

- General. (1) Systems must use only the analytical methods  specified in this section, or their equivalent as approved by EPA, to demonstrate com- pliance with the requirements of this subpart and with the requirements of subparts U and V of this part. These methods are effective for compliance monitoring February 16, 1999, unless a

#### Environmental Protection Agency	§ 141.131

different effective date is specified in this section or by the State.

(2)  The  following  documents  are  in- corporated  by  reference.  The  Director of  the  Federal  Register  approves  this incorporation  by  reference  in  accord- ance  with  5  U.S.C.  552(a)  and  1  CFR part  51.  Copies  may  be  inspected  at EPA’s   Drinking   Water   Docket,   1301 Constitution  Avenue,  NW.,  EPA  West, Room B102, Washington, DC 20460, or at the National Archives and Records Ad- ministration   (NARA).   For   information on  the  availability  of  this  material  at NARA, call 202–741–6030.  EPA  Method  552.1  is in  Methods  for  the  Determination  of Organic Compounds in Drinking Water- Supplement   II,   USEPA,   August   1992, EPA/600/R–92/129 (available through Na- tional   Information   Technical   Service (NTIS),   PB92–207703).   EPA   Methods 502.2, 524.2, 551.1, and 552.2 are in Meth- ods  for  the  Determination  of  Organic Compounds  in  Drinking  Water-Supple- ment III, USEPA, August 1995, EPA/600/ R–95/131	(available	through	NTIS, PB95–261616).  EPA Method 300.0  is in Methods for the Determination of Inor- ganic    Substances    in    Environmental Samples, USEPA, August 1993, EPA/600/ R–93/100	(available	through	NTIS, PB94–121811). EPA Methods 300.1 and

321.8 are in Methods for the Determina- tion of Organic and Inorganic Com- pounds in Drinking Water, Volume 1, USEPA, August 2000, EPA 815–R–00–014 (available through NTIS, PB2000– 106981). EPA Method 317.0, Revision 2.0, ‘‘Determination of Inorganic Oxyhalide Disinfection By-Products in Drinking Water Using Ion Chromatography with the Addition of a Postcolumn  Reagent for Trace Bromate Analysis,’’  USEPA, July 2001, EPA 815–B–01–001, EPA Meth- od 326.0, Revision 1.0,  ‘‘Determination of Inorganic Oxyhalide Disinfection By-Products in  Drinking  Water  Using Ion Chromatography Incorporating the Addition of a Suppressor Acidified Postcolumn Reagent  for  Trace  Bro- mate  Analysis,’’  USEPA,  June   2002, EPA 815–R–03–007, EPA Method 327.0, Revision 1.1, ‘‘Determination of  Chlo- rine Dioxide and Chlorite Ion in  Drink- ing Water  Using  Lissamine  Green  B and   Horseradish   Peroxidase   with   De-

tection	by	Visible Spectrophotometry,’’    USEPA,    May 2005, EPA 815–R–05–008 and EPA Method

552.3,  Revision  1.0,  ‘‘Determination  of Haloacetic	Acids	and	Dalapon	in Drinking	Water	by	Liquid-liquid Microextraction,     Derivatization,     and Gas    Chromatography    with    Electron Capture  Detection,’’  USEPA,  July  2003, EPA–815–B–03–002 can be accessed and downloaded  directly  on-line  . EPA  Method  415.3,  Revi- sion  1.1,  ‘‘Determination  of  Total  Or- ganic  Carbon  and  Specific  UV  Absorb- ance  at  254  nm  in  Source  Water  and Drinking     Water,’’     USEPA,     February 2005, EPA/600/R–05/055 can be accessed and   downloaded   directly   on-line

Standard Methods 4500–Cl D, 4500–Cl E, 4500–Cl F, 4500–Cl G, 4500–Cl H, 500–Cl I,

4500–ClO2   D,  4500–ClO2   E,  6251  B,  and

5910 B shall be followed in accordance with Standard Methods for the Exam- ination of Water and Wastewater, 19th or 20th Editions, American Public Health Association, 1995 and 1998, re- spectively. The cited methods pub- lished in either edition may be used. Standard Methods 5310 B, 5310 C, and 5310 D shall be followed in accordance with the Supplement to the 19th Edi- tion of Standard Methods for the Ex- amination of Water and Wastewater, or the Standard Methods for the Exam- ination of Water and Wastewater, 20th Edition, American Public Health Asso- ciation, 1996 and 1998, respectively. The cited methods published in either edi- tion may be used. Copies may be ob- tained  from  the  American  Public Health Association, 1015 Fifteenth Street, NW., Washington, DC 20005. Standard Methods 4500–Cl D–00, 4500–Cl E–00, 4500–Cl F–00, 4500–Cl G–00, 4500–Cl H–00, 4500–Cl I–00, 4500–ClO2 E–00, 6251 B–94, 5310 B–00, 5310 C–00, 5310 D–00 and

5910 B–00 are available or at EPA’s Water Docket. The year in which each method was approved by the Standard Methods Committee is designated by the last two digits in the method num- ber. The methods listed are the only Online versions that are IBR-approved. ASTM Methods D 1253–86 and D 1253–86 (Reapproved 1996) shall be followed in accordance  with  the  Annual  Book  of

#### § 141.131

ASTM Standards, Volume 11.01, Amer- ican Society for  Testing and  Materials International, 1996 or  any  ASTM  edi- tion containing  the  IBR-approved version of the method may  be  used. ASTM Method D1253–03 shall be fol- lowed in accordance with the  Annual Book  of  ASTM  Standards,   Volume 11.01, American Society for Testing and Materials International, 2004 or  any ASTM edition containing the IBR-ap- proved version of the method may be used. ASTM Method D 6581–00 shall be followed in accordance with the Annual Book  of  ASTM  Standards,   Volume 11.01,  American  Society  for  Testing  and

#### 40 CFR Ch. I (7–1–17 Edition)

Materials International, 2001 or any ASTM edition containing the IBR-ap- proved version of the method may be used; copies may be obtained from the American Society for Testing and Ma- terials International, 100 Barr Harbor Drive, West Conshohocken, PA 19428– 2959.

- Disinfection byproducts. (1) Sys- tems must measure disinfection by- products by the methods (as  modified by the footnotes) listed in the fol- lowing table or one of the alternative methods listed in appendix A to sub- part C of this part:

APPROVED METHODS FOR DISINFECTION BYPRODUCT COMPLIANCE MONITORING

| Contaminant and methodology 1 | EPA method | Standard method 2 | SM online 9 | ASTM method 3 |
| --- | --- | --- | --- | --- |
| TTHM P&T/GC/ElCD & PID ............. P&T/GC/MS ........................... LLE/GC/ECD ......................... HAA5 LLE (diazomethane)/GC/ECD SPE (acidic methanol)/GC/ ECD. LLE (acidic methanol)/GC/ ECD. Bromate Ion chromatography .............. Ion chromatography & post column reaction. IC/ICP–MS ............................. Chlorite Amperometric titration ........... Spectrophotometry ................ Ion chromatography .............. | 502.2 4. 524.2. 551.1. .......................... 552.1 5. 552.2, 552.3. 300.1 ..................... 317.0 Rev 2.0 6, 326.0 6. 321.8 6 7. .......................... 327.0 Rev 1.1 8. 300.0, 300.1, 317.0 Rev 2.0, 326.0. | 6251 B 5 ................ .......................... 4500–ClO2 E 8 ...... .......................... | 6251 B–94. .......................... 4500–ClO2 E–00 8. .......................... | D 6581–00 D 6581–00 |

1 P&T = purge and trap; GC = gas chromatography; ElCD = electrolytic conductivity detector; PID = photoionization detector; MS = mass spectrometer; LLE = liquid/liquid extraction; ECD = electron capture detector; SPE = solid phase extraction; IC = ion chromatography; ICP–MS = inductively coupled plasma/mass spectrometer.

2 19th and 20th editions of Standard Methods for the Examination of Water and Wastewater, 1995 and 1998, respectively, American Public Health Association; either of these editions may be used.

3 Annual Book of ASTM Standards, 2001 or any year containing the cited version of the method, Vol 11.01.

4 If TTHMs are the only analytes being measured in the sample, then a PID is not required.

5 The samples must be extracted within 14 days of sample collection.

6 Ion chromatography & post column reaction or IC/ICP-MS must be used for monitoring of bromate for purposes of dem- onstrating eligibility of reduced monitoring, as prescribed in § 141.132(b)(3)(ii).

7 Samples must be preserved at the time of sampling with 50 mg ethylenediamine (EDA)/L of sample and must be analyzed within 28 days.

8 Amperometric titration or spectrophotometry may be used for routine daily monitoring of chlorite at the entrance to the dis- tribution system, as prescribed in § 141.132(b)(2)(i)(A). Ion chromatography must be used for routine monthly monitoring of chlo- rite and additional monitoring of chlorite in the distribution system, as prescribed in § 141.132(b)(2)(i)(B) and (b)(2)(ii).

9 The Standard Methods Online version that is approved is indicated by the last two digits in the method number which is the year of approval by the Standard Method Committee. Standard Methods Online

- Analyses under this section for disinfection byproducts must be con- ducted by laboratories that have re- ceived certification by EPA or the State, except as specified under para- graph (b)(3) of this section. To receive certification to  conduct  analyses  for the DBP contaminants in §§ 141.64, 141.135, and subparts U and V of this part, the laboratory must:

- Analyze Performance Evaluation (PE) samples that are acceptable to EPA or the State at least once during each consecutive 12 month period by each method for which the laboratory desires certification.

- Until March 31, 2007, in these analyses of PE samples, the laboratory must     achieve     quantitative     results

#### Environmental Protection Agency	§ 141.131

within the acceptance limit on a min- imum of 80% of the analytes included in each PE sample. The acceptance limit is defined as the 95% confidence interval calculated around the mean of the PE study between a maximum and

minimum acceptance limit of 50% and

15% of the study mean.

- Beginning April 1, 2007, the lab- oratory must achieve quantitative re- sults on the PE sample analyses  that are within the following acceptance limits:

| DBP | Acceptance limits (percent of true value) | Comments |
| --- | --- | --- |
| TTHM | 20 20 20 20 40 | Laboratory must meet all 4 individual THM acceptance lim- its in order to successfully pass a PE sample for TTHM Laboratory must meet the acceptance limits for 4 out of 5 of the HAA5 compounds in order to successfully pass a PE sample for HAA5 |
| Chloroform ............................................. Bromodichloromethane .......................... Dibromochloromethane .......................... Bromoform ............................................. HAA5 Monochloroacetic Acid ........................... |  |  |
| Dichloroacetic Acid ................................ | 40 |  |
| Trichloroacetic Acid ............................... | 40 |  |
| Monobromoacetic Acid .......................... | 40 |  |
| Dibromoacetic Acid ................................ | 40 |  |
| Chlorite ................................................................. | 30 |  |
| Bromate ................................................................ | 30 |  |

- Beginning April 1, 2007, report quantitative data for concentrations at least as low as the ones listed in the following table for all DBP samples analyzed for compliance with §§ 141.64, 141.135, and subparts U and V of this part:

| DBP | Minimum re- porting level (mg/L) 1 | Comments |
| --- | --- | --- |
| TTHM 2 | 0.0010 | Applicable to monitoring as prescribed in § 141.132(b)(2)(1)(B) and (b)(2)(ii). Laboratories that use EPA Methods 317.0 Revision 2.0, 326.0 or 321.8 must meet a 0.0010 mg/L MRL for bro- mate. |
| Chloroform .................................................. |  |  |
| Bromodichloromethane .............................. | 0.0010 |  |
| Dibromochloromethane .............................. | 0.0010 |  |
| Bromoform .................................................. | 0.0010 |  |
| HAA5 2 |  |  |
| Monochloroacetic Acid ............................... | 0.0020 |  |
| Dichloroacetic Acid ..................................... | 0.0010 |  |
| Trichloroacetic Acid .................................... | 0.0010 |  |
| Monobromoacetic Acid ............................... | 0.0010 |  |
| Dibromoacetic Acid .................................... | 0.0010 |  |
| Chlorite ...................................................................... Bromate .................................................................... | 0.020 0.0050 or 0.0010 |  |

1 The calibration curve must encompass the regulatory minimum reporting level (MRL) concentration. Data may be reported for concentrations lower than the regulatory MRL as long as the precision and accuracy criteria are met by analyzing an MRL check standard at the lowest reporting limit chosen by the laboratory. The laboratory must verify the accuracy of the calibration curve at the MRL concentration by analyzing an MRL check standard with a concentration less than or equal to 110% of the MRL with each batch of samples. The measured concentration for the MRL check standard must be 50% of the expected value, if any field sample in the batch has a concentration less than 5 times the regulatory MRL. Method requirements to analyze higher con- centration check standards and meet tighter acceptance criteria for them must be met in addition to the MRL check standard re- quirement.

2 When adding the individual trihalomethane or haloacetic acid concentrations to calculate the TTHM or HAA5 concentrations, respectively, a zero is used for any analytical result that is less than the MRL concentration for that DBP, unless otherwise speci- fied by the State.

- A party approved by EPA or the State must measure daily chlorite samples at the entrance to the dis- tribution system.

- Disinfectant residuals. (1) Systems must    measure    residual    disinfectant

concentration for free chlorine, com- bined chlorine (chloramines), and chlo- rine dioxide by the methods listed  in the following table or one of the alter- native methods listed in appendix A to subpart C of this part:

#### § 141.131

40 CFR Ch. I (7–1–17 Edition)

| Methodology | SM (19th or 20th ed) | SM Online 2 | ASTM method | EPA method | Residual measured 1 |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Free Cl2 | Com- bined Cl2 | Total Cl2 | ClO2 |
| Amperometric Titration .......... | 4500–Cl D | 4500–Cl D–00 | D 1253–86 | 327.0 Rev 1.1 | X | X | X | X |
|  |  |  | (96), 03 |  |  |  |  |  |
| Low Level Amperometric Ti- | 4500–Cl E | 4500–Cl E–00 |  |  |  |  | X |  |
| tration. |  |  |  |  |  |  |  |  |
| DPD Ferrous Titrimetric ........ | 4500–Cl F | 4500–Cl F–00 |  |  | X | X | X |  |
| DPD Colorimetric .................. | 4500–Cl G | 4500–Cl G–00 |  |  | X | X | X |  |
| Syringaldazine (FACTS) ....... | 4500–Cl H | 4500–Cl H–00 |  |  | X |  |  |  |
| Iodometric Electrode ............. | 4500–Cl I | 4500–Cl I–00 |  |  |  |  | X |  |
| DPD ....................................... | 4500–ClO2 D |  |  |  |  |  |  |  |
| Amperometric Method II ........ | 4500–ClO2 E | 4500–ClO2 E– |  |  |  |  |  | X |
|  |  | 00 |  |  |  |  |  |  |
| Lissamine Green |  |  |  |  |  |  |  | X |
| Spectrophotometric. |  |  |  |  |  |  |  |  |

1 X indicates method is approved for measuring specified disinfectant residual. Free chlorine or total chlorine may be measured for demonstrating compliance with the chlorine MRDL and combined chlorine, or total chlorine may be measured for dem- onstrating compliance with the chloramine MRDL.

2 The Standard Methods Online version that is approved is indicated by the last two digits in the method number which is the year of approval by the Standard Method Committee. Standard Methods Online are available

- If approved by the State, systems may also measure residual disinfectant concentrations	for	chlorine, chloramines, and chlorine dioxide by using DPD colorimetric test kits.

- A party approved by EPA or the State must measure residual disinfect- ant concentration.

- Additional analytical methods. Sys- tems required to analyze parameters not included in paragraphs (b) and (c) of this section must use the following methods or one of the alternative methods listed in appendix A to sub- part C of this part. A party approved by EPA or the State must measure these parameters.

  - Alkalinity. All methods allowed  in

§ 141.89(a) for measuring alkalinity.

  - Bromide. EPA Methods 300.0, 300.1,

317.0   Revision   2.0,   326.0,   or   ASTM   D 6581–00.

  - Total Organic Carbon (TOC). Standard Method 5310 B or 5310 B–00 (High-Temperature Combustion Meth- od) or Standard Method 5310 C or 5310 C–00 (Persulfate-Ultraviolet or Heated- Persulfate Oxidation Method) or Stand- ard Method 5310 D or 5310 D–00 (Wet-Ox- idation Method) or EPA Method 415.3 Revision 1.1. Inorganic carbon must be removed from the samples prior to analysis. TOC samples may not be fil- tered prior to analysis. TOC samples must be acidified at the time of sample collection to achieve pH less than or equal to 2 with minimal addition of the acid specified in the method or by the instrument      manufacturer.      Acidified

TOC samples must be analyzed  within 28 days.

  - Specific Ultraviolet Absorbance (SUVA). SUVA is equal to the UV ab- sorption at 254nm (UV254) (measured in m-1 divided by the dissolved organic carbon (DOC) concentration (measured as mg/L). In order to determine SUVA, it is necessary to separately measure UV254 and DOC.  When  determining SUVA, systems must use the methods stipulated in paragraph (d)(4)(i) of this section to measure DOC and the meth- od stipulated in paragraph (d)(4)(ii) of this section to measure UV254.  SUVA must be determined on water prior to the addition  of  disinfectants/oxidants by the system. DOC and UV254 samples used to determine a SUVA  value  must be taken at the same time and at the same  location.

- Dissolved Organic Carbon (DOC). Standard Method 5310 B or 5310 B–00 (High-Temperature Combustion Meth- od) or Standard Method 5310 C or 5310 C–00 (Persulfate-Ultraviolet or Heated- Persulfate Oxidation Method) or Stand- ard Method 5310 D or 5310 D–00 (Wet-Ox- idation Method) or EPA Method 415.3 Revision 1.1. DOC samples must be fil- tered through the 0.45 m pore-diame- ter filter as soon as practical after sampling, not to exceed 48 hours. After filtration, DOC samples must be acidi- fied to achieve pH less than or equal to

2 with minimal addition of the acid specified in the method or by the in- strument manufacturer. Acidified DOC samples  must  be  analyzed  within  28

#### Environmental Protection Agency	§ 141.132

days of sample collection. Inorganic carbon must be removed from the sam- ples prior to analysis. Water passed through the filter prior to filtration of the sample must serve as the filtered blank. This filtered blank must be ana- lyzed using procedures identical to those used for analysis of the samples and must meet the following criteria: DOC <0.5 mg/L.

- Ultraviolet Absorption at 254 nm (UV254). Standard Method 5910 B or 5910 B–00  (Ultraviolet  Absorption  Method) or EPA Method 415.3 Revision 1.1. UV absorption must be measured at 253.7 nm (may be rounded off to 254 nm). Prior  to  analysis,  UV254   samples   must be filtered through a 0.45 m pore-di- ameter filter. The pH of UV254 samples may not be adjusted. Samples must be analyzed as soon as practical after sampling, not to exceed 48 hours.

  - pH.   All   methods   allowed   in

§ 141.23(k)(1) for measuring pH.

  - Magnesium.  All  methods  allowed in § 141.23(k)(1) for measuring magne- sium.

[63 FR 69466, Dec. 16, 1998, as amended at 66

FR 3776, Jan. 16, 2001; 71 FR 479, Jan. 4, 2006;

71  FR 37168,  June 29,  2006;  74  FR 30958,  June

29, 2009]

##### § 141.132   Monitoring requirements.

- General requirements. (1) Systems must take all samples during normal operating  conditions.

- Systems may consider multiple wells drawing water from a single aqui- fer as one treatment plant for deter- mining the minimum number of TTHM and HAA5 samples required, with State approval in accordance with criteria developed under § 142.16(h)(5) of this chapter.

- Failure to monitor in accordance with the monitoring plan required under paragraph (f) of this section is a monitoring violation.

- Failure to monitor will be treated as a violation for the entire period cov- ered by the annual average where com- pliance is based on a running annual average of monthly or quarterly sam- ples or averages and the system’s fail- ure to monitor makes it impossible to determine compliance with MCLs or MRDLs.

- Systems may use only data col- lected under the provisions of this sub- part to qualify for reduced monitoring.

- Monitoring requirements for dis- infection byproducts—(1)  TTHMs and HAA5—(i) Routine monitoring. Systems must monitor at the  frequency indi- cated in the following table:

ROUTINE MONITORING FREQUENCY FOR TTHM AND HAA5

| Type of system | Minimum monitoring frequency | Sample location in the distribution system |
| --- | --- | --- |
| Subpart H system serving at least 10,000 persons. Subpart H system serving from 500 to 9,999 persons. Subpart H system serving fewer than 500 persons. System using only ground water not under direct influ- ence of surface water using chemical disinfectant and serving at least 10,000 per- sons. | Four water samples per quar- ter per treatment plant. One water sample per quarter per treatment plant. One sample per year per treatment plant during month of warmest water temperature. One water sample per quarter per treatment plant 2. | At least 25 percent of all samples collected each quarter at locations representing maximum residence time. Remain- ing samples taken at locations representative of at least average residence time in the distribution system and rep- resenting the entire distribution system, taking into account number of persons served, different sources of water, and different treatment methods. 1 Locations representing maximum residence time. 1 Locations representing maximum residence time. 1 If the sample (or average of annual samples, if more than one sample is taken) exceeds the MCL, the system must in- crease monitoring to one sample per treatment plant per quarter, taken at a point reflecting the maximum residence time in the distribution system, until the system meets cri- teria in paragraph (b)(1)(iv) of this section. Locations representing maximum residence time. 1 |

#### § 141.132

40 CFR Ch. I (7–1–17 Edition)

ROUTINE MONITORING FREQUENCY FOR TTHM AND HAA5—Continued

| Type of system | Minimum monitoring frequency | Sample location in the distribution system |
| --- | --- | --- |
| System using only ground water not under direct influ- ence of surface water using chemical disinfectant and serving fewer than 10,000 persons. | One sample per year per treatment plant 2 during month of warmest water temperature. | Locations representing maximum residence time. 1 If the sample (or average of annual samples, if more than one sample is taken) exceeds the MCL, the system must in- crease monitoring to one sample per treatment plant per quarter, taken at a point reflecting the maximum residence time in the distribution system, until the system meets cri- teria in paragraph (b)(1)(iv) of this section. |

1 If a system elects to sample more frequently than the minimum required, at least 25 percent of all samples collected each quarter (including those taken in excess of the required frequency) must be taken at locations that represent the maximum resi- dence time of the water in the distribution system. The remaining samples must be taken at locations representative of at least average residence time in the distribution system.

2 Multiple wells drawing water from a single aquifer may be considered one treatment plant for determining the minimum num- ber of samples required, with State approval in accordance with criteria developed under § 142.16(h)(5) of this chapter.

- Systems may reduce monitoring, except as otherwise provided, in accord- ance with the following table:

REDUCED MONITORING FREQUENCY FOR TTHM AND HAA5

| If you are a . . . | You may reduce monitoring if you have monitored at least one year and your . . . | To this level |
| --- | --- | --- |
| Subpart H system serving at least 10,000 persons which has a source water annual average TOC level, before any treatment, 4.0 mg/L. Subpart H system serving from 500 to 9,999 persons which has a source water annual average TOC level, before any treatment, 4.0 mg/L. System using only ground water not under direct influ- ence of surface water using chemical disinfectant and serving at least 10,000 per- sons. System using only ground water not under direct influ- ence of surface water using chemical disinfectant and serving fewer than 10,000 persons. | TTHM annual average 0.040 mg/L and HAA5 annual av- erage 0.030 mg/L. TTHM annual average 0.040 mg/L and HAA5 annual av- erage 0.030 mg/L. TTHM annual average 0.040 mg/L and HAA5 annual av- erage 0.030 mg/L. TTHM annual average 0.040 mg/L and HAA5 annual av- erage 0.030 mg/L for two consecutive years OR TTHM annual average 0.020 mg/L and HAA5 an- nual average 0.015 mg/L for one year. | One sample per treatment plant per quarter at distribution system location reflecting maximum residence time. One sample per treatment plant per year at distribution sys- tem location reflecting maximum residence time during month of warmest water temperature. NOTE: Any Subpart H system serving fewer than 500 persons may not reduce its monitoring to less than one sample per treatment plant per year. One sample per treatment plant per year at distribution sys- tem location reflecting maximum residence time during month of warmest water temperature One sample per treatment plant per three year monitoring cycle at distribution system location reflecting maximum residence time during month of warmest water tempera- ture, with the three-year cycle beginning on January 1 fol- lowing quarter in which system qualifies for reduced moni- toring. |

- Monitoring requirements for source water TOC. In order to qualify for re- duced monitoring for TTHM and HAA5 under paragraph (b)(1)(ii) of this sec- tion, subpart H systems not moni- toring under the  provisions of para- graph (d) of this section must take monthly TOC samples every 30 days at a location prior to any treatment, be- ginning April 1, 2008 or earlier, if speci- fied by the State. In addition  to  meet- ing other criteria for reduced moni- toring in paragraph (b)(1)(ii) of this section, the  source  water TOC  running annual average must be 4.0 mg/L (based on the most recent four quarters

of monitoring) on a continuing basis at each treatment plant to reduce or re- main on reduced monitoring for TTHM and HAA5. Once qualified for reduced monitoring for TTHM and HAA5 under paragraph (b)(1)(ii) of this section, a system may reduce source water TOC monitoring to quarterly TOC samples taken every 90 days at a location prior to  any  treatment.

- Systems on a reduced monitoring schedule may remain on that reduced schedule as long as the average of all samples taken in the year (for systems which must monitor quarterly) or the result of the sample (for systems which

#### Environmental Protection Agency	§ 141.132

must monitor no more frequently than annually) is no more than 0.060 mg/L and 0.045 mg/L for TTHMs and HAA5, respectively. Systems that do not meet these  levels  must  resume   monitoring at  the  frequency  identified  in  para- graph (b)(1)(i) of this section (minimum monitoring frequency column) in the quarter immediately following the monitoring period in which the system exceeds 0.060 mg/L or 0.045 mg/L for TTHMs and HAA5, respectively. For systems using only ground water not under the direct influence of surface water and serving fewer than 10,000 per- sons, if either the TTHM annual aver- age is >0.080 mg/L or the HAA5 annual average is >0.060 mg/L, the  system must go to the increased monitoring identified in paragraph (b)(1)(i) of this section  (sample   location   column)   in the quarter immediately following the monitoring period in which the system exceeds 0.080 mg/L or 0.060 mg/L for TTHMs  or  HAA5  respectively.

- Systems on increased monitoring may return to routine monitoring if, after at least one year of monitoring their TTHM annual average is 0.060 mg/L and their HAA5 annual average is

0.045 mg/L.

- The State  may  return  a system to routine monitoring at the State’s discretion.

  - Chlorite. Community and nontran- sient noncommunity water systems using chlorine dioxide, for disinfection or oxidation, must conduct monitoring for chlorite.

    - Routine monitoring. (A) Daily moni- toring. Systems must take daily sam- ples at the entrance to the distribution system. For any daily sample that ex- ceeds the chlorite MCL, the system must take additional samples in the distribution system the following day at the locations required by paragraph (b)(2)(ii) of this section, in addition to the sample required at the entrance to the distribution system.

(B) Monthly monitoring. Systems must take a three-sample set each month in the distribution system. The system must take one sample at each of the following locations: near the first cus- tomer, at a location representative of average residence time, and at a loca- tion reflecting maximum residence time  in  the  distribution  system.  Any

additional routine sampling must be conducted in the same manner (as three-sample sets, at the specified loca- tions). The system may use the results of additional monitoring conducted under paragraph (b)(2)(ii) of this sec- tion to meet the requirement for moni- toring in this paragraph.

    - Additional monitoring. On each day following a routine sample monitoring result that exceeds the chlorite MCL at the entrance to the distribution sys- tem, the system is required to take three chlorite distribution system sam- ples at the following locations: as close to the first customer as possible, in a location representative of average resi- dence time, and as close to the end of the distribution system as possible (re- flecting maximum residence time in the distribution system).

    - Reduced monitoring. (A) Chlorite monitoring at the entrance to the dis- tribution system required by paragraph (b)(2)(i)(A) of this section may not be reduced.

(B) Chlorite monitoring in the dis- tribution system required by paragraph (b)(2)(i)(B) of this section may be re- duced to one three-sample set per quar- ter after one year of monitoring where no individual chlorite sample taken in the distribution system under para- graph (b)(2)(i)(B) of this section has ex- ceeded the chlorite MCL and the sys- tem has not been required to conduct monitoring under paragraph (b)(2)(ii) of this section. The system may  remain on the reduced monitoring schedule until either any of the three individual chlorite samples taken quarterly in the distribution system under paragraph (b)(2)(i)(B) of this section exceeds the chlorite MCL or the system is required to conduct monitoring under paragraph (b)(2)(ii) of this section, at which time the system must revert to routine monitoring.

  - Bromate—(i) Routine monitoring. Community and nontransient  non- community systems using ozone, for disinfection or oxidation, must take one sample per month for each treat- ment plant in the system using ozone. Systems must take samples  monthly at the entrance to the distribution sys- tem while the ozonation system is op- erating under normal conditions.

#### § 141.132

(ii) Reduced monitoring. (A) Until March 31, 2009, systems required to analyze for bromate may reduce moni- toring  from  monthly  to  quarterly,  if the system’s average source water bro- mide concentration is less than 0.05 mg/L based on representative monthly bromide measurements for one year. The system  may  remain on  reduced bromate monitoring until the running annual average source water bromide concentration, computed quarterly, is equal to or greater than 0.05  mg/L based on representative monthly meas- urements. If the running annual aver- age source water bromide concentra- tion is 0.05 mg/L, the system must re- sume routine monitoring required by paragraph (b)(3)(i) of this section in the following  month.

(B) Beginning April 1, 2009, systems may no longer use the provisions of paragraph (b)(3)(ii)(A) of this section to qualify for reduced monitoring. A sys- tem required to analyze for bromate may reduce monitoring from  monthly to quarterly, if the system’s running annual average bromate  concentration is 0.0025 mg/L based on monthly bro- mate measurements under paragraph (b)(3)(i) of this section for the most re- cent four quarters, with samples ana- lyzed using Method 317.0 Revision 2.0,

326.0 or 321.8. If a system has qualified for reduced bromate monitoring under paragraph (b)(3)(ii)(A) of this  section, that system may remain on reduced monitoring as long as the running an- nual average of quarterly  bromate samples 0.0025 mg/L based on samples analyzed using Method  317.0  Revision 2.0, 326.0, or 321.8. If the running annual average      bromate      concentration      is

>0.0025 mg/L, the system must resume routine monitoring required by para- graph (b)(3)(i) of this section.

- Monitoring requirements for dis- infectant residuals—(1) Chlorine and chloramines—(i)  Routine   monitoring. Until March 31, 2016, community and non-transient non-community water systems  that  use  chlorine   or chloramines must measure the residual disinfectant level in the distribution system at the same point in the dis- tribution system and at  the  same  time as total coliforms are sampled, as spec- ified in § 141.21. Beginning April 1, 2016, community     and     non-transient     non-

#### 40 CFR Ch. I (7–1–17 Edition)

community water systems that use chlorine or chloramines must measure the residual disinfectant level in the distribution system at the  same  point in the distribution system  and  at  the same time as total coliforms are sam- pled, as specified in §§ 141.854 through 141.858. Subpart H systems of this part may use the results of residual dis- infectant concentration sampling con- ducted under § 141.74(b)(6)(i) for unfiltered systems or § 141.74(c)(3)(i) for systems which filter, in lieu of taking separate   samples.

(ii) Reduced monitoring. Monitoring may not be reduced.

(2) Chlorine dioxide—(i) Routine moni- toring. Community, nontransient  non- community, and transient noncommu- nity water systems that use chlorine dioxide for disinfection or oxidation must take daily samples at the en- trance to the distribution system. For any daily sample that exceeds the MRDL, the system must take samples in the distribution system the fol- lowing day at the locations required by paragraph (c)(2)(ii) of this section, in addition to the sample required at the entrance to the distribution system.

- Additional monitoring. On each day following a routine sample monitoring result that exceeds the MRDL, the sys- tem is required to take three chlorine dioxide distribution system samples.  If chlorine dioxide or chloramines are used to maintain a disinfectant resid- ual in the distribution system, or if chlorine is used to maintain a dis- infectant residual in the distribution system and there are no disinfection addition points after the entrance to the distribution system (i.e., no booster chlorination), the system must take three samples as close to the first cus- tomer as possible, at intervals of at least six hours. If chlorine is used to maintain a disinfectant residual in the distribution system and there  are  one or more disinfection addition points after the entrance to the distribution system (i.e., booster chlorination), the system must take one  sample  at  each of the following locations: as close  to the first customer as possible, in a lo- cation representative of average resi- dence time, and as close to the end of

#### Environmental Protection Agency	§ 141.133

the distribution system as possible (re- flecting maximum residence time in the distribution system).

- Reduced monitoring. Chlorine di- oxide monitoring may not be reduced.

- Monitoring requirements for dis- infection byproduct precursors (DBPP)—

- Routine monitoring. Subpart H sys- tems which use conventional filtration treatment (as defined in § 141.2) must monitor each treatment plant for  TOC no later than the point of combined fil- ter effluent turbidity monitoring and representative of the treated water. All systems required to monitor under this paragraph (d)(1) must also monitor for TOC in the source water prior to any treatment at the same time as moni- toring for TOC in the treated water. These samples (source water and treat- ed water) are referred to as paired sam- ples. At the same time as the source water sample is taken, all  systems must monitor for alkalinity in the source water prior to any treatment. Systems must take one paired sample and one source water alkalinity sample per month per plant at a time rep- resentative of normal operating condi- tions and influent water quality.

- Reduced monitoring. Subpart H sys- tems with an average  treated  water TOC of less than 2.0 mg/L for two con- secutive years, or less than 1.0 mg/L for one year, may reduce monitoring for both TOC and alkalinity to one paired sample and one source water alkalinity sample per plant per quarter. The sys- tem must revert to routine monitoring in the month following the quarter when the annual average treated water TOC 2.0 mg/L.

- Bromide. Systems required to ana- lyze for bromate may reduce bromate monitoring from monthly to once per quarter, if the system  demonstrates that the average source water bromide concentration is less than 0.05 mg/L based upon representative monthly measurements for one year. The sys- tem must continue bromide monitoring to remain on reduced bromate moni- toring.

- Monitoring plans. Each system re- quired to monitor under this subpart must develop and implement a moni- toring plan. The system must maintain the plan and make it available for in- spection by the State and the general

public no  later than 30  days  following the    applicable    compliance    dates    in

§ 141.130(b). All Subpart H systems serv- ing more than 3300 people must submit a copy of the monitoring plan to the State no later than the date of the first report required under § 141.134. The State may also require the plan to be submitted by any other system. After review, the State may  require  changes in any plan elements. The plan must include  at  least  the  following  elements.

- Specific locations and schedules for collecting samples for any param- eters included in this subpart.

- How the system will calculate compliance with MCLs, MRDLs, and treatment techniques.

- If approved for monitoring as a consecutive system, or if  providing water to  a  consecutive  system,  under the provisions of § 141.29, the sampling plan must reflect  the  entire  distribu- tion   system.

[63 FR 69466, Dec. 16, 1998, as amended at 66

FR 3776,  Jan. 16,  2001;  69  FR 38856,  June 29,

2004; 71 FR 482, Jan. 4, 2006; 78 FR 10348, Feb.

13, 2013]

##### § 141.133   Compliance requirements.

  - General requirements. (1) Where compliance is based on a running an- nual average of monthly or quarterly samples or averages and the system fails to monitor for TTHM, HAA5, or bromate, this failure to monitor will be treated as a monitoring violation for the entire period covered by the annual average. Where compliance is based on a running annual average of  monthly or quarterly samples or averages and the system failure to monitor makes it impossible to determine compliance with MRDLs for chlorine and chloramines, this failure  to  monitor will be treated as a monitoring viola- tion for the entire period covered  by the annual average.

- All samples taken and analyzed under the provisions of this subpart must be included in determining com- pliance, even if that number is greater than the minimum required.

- If, during the first year of moni- toring under § 141.132, any individual quarter’s average will cause the run- ning annual average of that system to exceed the MCL for total trihalomethanes,        haloacetic        acids

#### § 141.133

(five), or bromate; or the MRDL for chlorine or chloramine, the system is out of compliance at the end of that quarter.

  - Disinfection byproducts—(1) TTHMs and HAA5. (i) For systems monitoring quarterly,  compliance  with  MCLs  in

§ 141.64 must be based on a running an- nual arithmetic average, computed quarterly, of quarterly arithmetic averages of all samples collected by the system as prescribed by § 141.132(b)(1).

- For systems monitoring less fre- quently than quarterly, systems dem- onstrate MCL compliance if the aver- age of samples taken that year  under the provisions of § 141.132(b)(1) does not exceed the MCLs in § 141.64. If the aver- age of these samples exceeds the MCL, the system must increase  monitoring to once per quarter per  treatment plant and such a system is not in viola- tion of the MCL until it has completed one year of quarterly monitoring, un- less the result of fewer than four quar- ters of monitoring will cause the run- ning annual average to exceed  the MCL, in which case the system is in violation at the end of that quarter. Systems required to increase moni- toring frequency to quarterly moni- toring must calculate compliance by including the sample which triggered the increased monitoring plus the fol- lowing three quarters of monitoring.

- If the running annual arithmetic average of quarterly averages covering any consecutive four-quarter period ex- ceeds the MCL, the system is in viola- tion of the MCL and must notify the public pursuant to § 141.32 or § 141.202, whichever is effective for your system, in addition to reporting to the State pursuant to § 141.134.

- If a PWS fails to complete four consecutive quarters of monitoring, compliance with the MCL for the last four-quarter compliance period must be based on an average of the available data.

  - Bromate. Compliance must be based on a running annual arithmetic average, computed quarterly, of monthly samples (or, for months in which the system takes more than one sample, the average f all samples taken during the month) collected by the sys- tem as prescribed by § 141.132(b)(3). If the  average  of  samples  covering  any

#### 40 CFR Ch. I (7–1–17 Edition)

consecutive four-quarter period ex- ceeds the MCL, the system is in viola- tion of the MCL and must notify the public pursuant to subpart Q, in addi- tion to reporting to the State pursuant to § 141.134. If a PWS fails to complete

12 consecutive months’ monitoring, compliance with the MCL for the last four-quarter compliance  period  must be based on an average of the available data.

  - Chlorite. Compliance must be based on an arithmetic average of each three sample set taken in the distribu- tion      system      as      prescribed      by

§ 141.132(b)(2)(i)(B)   and   § 141.132(b)(2)(ii).

If the arithmetic average of any three sample set exceeds the MCL, the sys- tem is in violation of the MCL and must notify the public pursuant to sub- part Q, in addition to reporting to the State pursuant to § 141.134.

  - Disinfectant residuals—(1) Chlorine and chloramines. (i) Compliance must be based on a running annual arithmetic average, computed quarterly, of monthly averages of all samples col- lected       by       the       system       under

§ 141.132(c)(1). If the average covering any consecutive four-quarter period ex- ceeds the MRDL, the system is in vio- lation of the MRDL and must  notify the public pursuant to subpart Q, in ad- dition to reporting to the State  pursu- ant to § 141.134.

(ii) In cases where systems switch be- tween the use of chlorine and chloramines for residual disinfection during the year, compliance must be determined by including together all monitoring results of both chlorine and chloramines in calculating compliance. Reports submitted pursuant to § 141.134 must clearly indicate which residual disinfectant was analyzed for each sample.

- Chlorine dioxide. (i) Acute viola- tions. Compliance must be based on consecutive daily samples collected by the system under § 141.132(c)(2). If any daily sample taken at the entrance  to the distribution system exceeds the MRDL, and on the following day  one (or more) of the three samples taken in the distribution system exceed the MRDL,  the  system  is  in  violation   of the MRDL and must take immediate corrective action to lower the level of chlorine  dioxide  below  the  MRDL  and

#### Environmental Protection Agency	§ 141.134

must notify the public pursuant to the procedures for acute health risks in subpart Q in addition to reporting  to the State pursuant to § 141.134. Failure to take samples in the distribution sys- tem the day following an exceedance of the chlorine dioxide MRDL at the en- trance to the distribution system will also be considered an MRDL violation and the system must  notify  the  public of the violation in accordance with the provisions for acute violations under subpart Q in addition to reporting  to the State pursuant to § 141.134.

(ii) Nonacute violations. Compliance must be based on consecutive daily samples collected by the system under

§ 141.132(c)(2). If any two consecutive daily samples taken at the entrance to the distribution system exceed  the MRDL and all distribution system samples  taken  are  below  the  MRDL, the system is in violation of the MRDL and must take corrective action to lower the level of chlorine dioxide below the MRDL at the point of sam- pling and will notify the public  pursu- ant to the procedures for nonacute health risks in subpart Q in addition to reporting   to   the   State   pursuant   to

§ 141.134. Failure to monitor at the en- trance to  the  distribution  system  the day following an exceedance of the chlorine dioxide MRDL at  the  entrance to the distribution system is also  an MRDL violation and the system must notify the public of the violation in ac- cordance with the provisions for nonacute violations under § 141.32(e)(78) in addition to reporting to the State pursuant to § 141.134.

  - Disinfection byproduct precursors (DBPP). Compliance must be deter- mined as specified by § 141.135(c). Sys- tems may begin monitoring to deter- mine whether Step 1 TOC removals can be met 12 months prior to the compli- ance  date  for  the  system.  This  moni-

toring is not required and failure to monitor during this period is not a vio- lation. However, any system that does not monitor during this  period,  and then determines in the first 12 months after the compliance date that it is not able to meet the Step 1 requirements in

§ 141.135(b)(2) and must therefore apply for alternate minimum TOC removal (Step 2) requirements, is not eligible for retroactive approval of alternate minimum TOC removal (Step 2) re- quirements   as   allowed   pursuant   to

§ 141.135(b)(3) and is in violation. Sys- tems  may  apply  for  alternate  min- imum TOC  removal  (Step  2)  require- ments any time after  the  compliance date.  For  systems  required   to   meet Step 1 TOC removals, if the value cal- culated under § 141.135(c)(1)(iv) is less than 1.00, the system is in  violation  of the treatment  technique  requirements and must notify the public pursuant to subpart Q of this part, in addition to reporting    to    the    State    pursuant    to

§ 141.134.

[63 FR 69466, Dec. 16, 1998, as amended at 65

FR  26022,  May  4,  2000;  65  FR  40521,  June  30,

2000;  66  FR 3777,  Jan. 16,  2001;  69  FR 38856,

June 29, 2004; 71 FR 482, Jan. 4, 2006]

##### § 141.134   Reporting and recordkeeping requirements.

- Systems required to sample quar- terly  or  more  frequently   must   report to the State within 10 days after  the end of each quarter in which samples were collected, notwithstanding the provisions of § 141.31. Systems  required to sample less frequently  than  quar- terly   must   report   to   the   State   within

10 days after the end of each moni- toring period in which samples were collected.

- Disinfection byproducts. Systems must report the information specified in the following table:

If you are a * * *

You must report * * *

- System monitoring for TTHMs and HAA5 under the require-   (i) The number of samples taken during the last quarter.

ments of § 141.132(b) on a quarterly or more frequent basis.     (ii) The location, date, and result of each sample taken during

the last quarter.

  - The  arithmetic  average  of  all  samples  taken  in  the  last quarter.

  - The annual arithmetic average of the quarterly arithmetic averages of this section for the last four quarters.

  - Whether, based on § 141.133(b)(1), the MCL was violated.

#### § 141.134

40 CFR Ch. I (7–1–17 Edition)

| If you are a * * * | You must report * * * |
| --- | --- |
| System monitoring for TTHMs and HAA5 under the require- ments of § 141.132(b) less frequently than quarterly (but as least annually). System monitoring for TTHMs and HAA5 under the requriements of § 141.132(b) less frequently than annually. System monitoring for chlorite under the requirements of § 141.132(b). System monitoring for bromate under the requirements of § 141.132(b). | The number of samples taken during the last year. The location, date, and result of each sample taken during the last monitoring period. The arithmetic average of all samples taken over the last year. Whether, based on § 141.133(b)(1), the MCL was violated. The location, date, and result of each sample taken Whether, based on § 141.133(b)(1), the MCL was violated. The number of entry point samples taken each month for the last 3 months. The location, date, and result of each sample (both entry point and distribution system) taken during the last quarter. For each month in the reporting period, the arithmetic aver- age of all samples taken in each three samples set taken in the distribution system. Whether, based on § 141.133(b)(3), the MCL was violated, in which month, and how many times it was violated each month. The number of samples taken during the last quarter. The location, date, and result of each sample taken during the last quarter. The arithmetic average of the monthly arithmetic averages of all samples taken in the last year. Whether, based on § 141.133(b)(2), the MCL was violated. |

1 The State may choose to perform calculations and determine whether the MCL was exceeded, in lieu of having the system report that information

- Disinfectants. Systems must report the information specified in the following table:

| If you are a * * * | You must report * * * |
| --- | --- |
| System monitoring for chlorine or chloramines under the re- quirements of § 141.132(c). System monitoring for chlorine dioxide under the require- ments of § 141.132(c). | The number of samples taken during each month of the last quarter. The month arithmetic average of all samples taken in each month for the last 12 months. The arithmetic average of the monthly averages for the last 12 months. Whether, based on § 141.133(c)(1), the MRD was violated. The dates, result, and locations of samples taken during the last quarter. Whether, based on § 141.133(c)(2), the MRDL was violated. Whether the MRDL was exceeded in any two consecutive daily samples and whether the resulting violation was acuate or nonacute. |

1 The State may choose to perform calculations and determine whether the MRDL was exceeded, in lieu of having the system report that information.

- Disinfection byproduct precursors and enhanced coagulation or enhanced soft- ening. Systems must report the information specified in the following table:

#### 40 CFR Ch. I (7–1–17 Edition)

the Regional Administrator shall ei- ther deny the petition or recommend to the Administrator that the initial determination that a project may con- taminate the aquifer be vacated. Upon receipt of a recommendation from the Regional Administrator that a deter- mination be vacated, the Adminis- trator shall either deny the petition or order that the initial determination be vacated. The final decision regarding a petition shall be published in the FED- ERAL REGISTER with an accompanying statement of reasons.

##### § 149.111   Funding	to	redesigned projects.

After publication of a decision that a proposed project may contaminate a sole or principal source aquifer in a designated area through its recharge zone so as to create a significant haz- ard to public health, a commitment for Federal financial assistance may be en- tered into, if authorized under another provision of law, to plan or redesign such project to assure that it will not so contaminate the aquifer.